## Slide 1: NCS5500/5700
Akshaya Kumar Sankaran
MIG TME
19 Jan 2021
ASIC Flexibility / MDB Profiles - Demo

## Slide 2: Cisco Disclaimer
Many of the products and features described herein remain in varying stages of development and will be offered on a when-and-if-available basis.
This roadmap is subject to change at the sole discretion of Cisco, and Cisco will have no liability for delay in the delivery or failure to deliver any of the products or features set forth in this document.
Some of the product information listed in this document is highly Cisco confidential and customer is under NDA with Cisco.

## Slide 3: Services scale requirements
Content Provider
Mobile Packet Core/ Broadband
Private Cloud
Peering /
Direct Connect
Public Cloud
Core
Aggregation
Residential
Business
Mobile
Cable
FTTH
Mobile Backhaul
Metro Ethernet
Aggregation
Business Services
L2 Services – P2P, P2MP (VPWS/VPLS/EVPN)
Higher MAC Table
MPLS services label /SRTE/SRv6
Bridge domain/ BVI
L2 Sub-interface
Aggregation
Mobile Services
L3 Services – VRF, L3VPN
BGP LU
L3 Sub-interface
ARP scale
SRTE/SRv6 PIDs
Core & Peering
LSR & Internet scale
IPv4/ IPv6 L3 Route Table
Multicast route

## Slide 4
Content Provider
Private Cloud
Peering /
Direct Connect
Public Cloud
NCS5504/08/16
NC57 -SE Line cards
NCS-57B1 -SE
NCS-57C3 -SE
NCS5504/08/16
NC57 Line card
NCS-57B1
NCS-57C3
NCS-57B1
NCS-57C3
NCS-57C3
Core
Aggregation
Pre-Aggregation
NCS 5504/08/16
Modular: up to 9.6T/slot
153.6Tb System
Fixed: Up to 4.8T
NCS 57B1
NCS 57C3
Fixed: Up to 4T
NC57-24DD
NCS57-18DD-SE
NC57-36H-SE
NC57-36H6D-S
NCS-57B1-6D24H
NCS-57B1-5D24H-SE
NCS-57C3-MOD
NCS-57C3-MOD-SE
NC57-MPA-2D4H
Residential
Business
Mobile
Cable
FTTH
Mobile Backhaul
Metro Ethernet
High Scale Converged SDN Network
Unique services / scale for different use cases
Same underlying ASIC
Mobile Packet Core/ Broadband
J2
J2c
L3 Profile
L2 Profile
Q2A
J2C+
*Roadmap
Q2C
*Roadmap

## Slide 5: MDB Profiles in J2
Modular Database
  Instead of dedicated memories
  Different allocation for different profiles
  LEM / LPM-KAPS / FEC / …
Off-chip
Buffers
Fabric Interface
Network Interface
Ingress
Egress
LPM
LEM
TCAM
STAT
FEC
PP
TM
PP
TM
On-chip Buffer
PP
TM
PP
TM
OTM
LPM
LEM
TCAM
STAT
FEC
OP
eTCAM
Fabric Interface
Network Interface
Ingress
Egress
PP
TM
PP
TM
PP
TM
PP
TM
HBM
On-chip Buffer
OTM
OP2
eTCAM
MDB

## Slide 6: MDB Profile resource carving
LEM
LPM
ISEM
L3 Profile
LEM
LPM
ISEM
L2 Profile

## Slide 7: MDB Profiles
L2Max-SE*
L3Max-SE
Today we have planned 4 MDB Profiles
Target platforms from XR7.6.1
Fixed
NCS-57B1-SE
NCS-57C3-SE
Modular
NC57-18DD-SE
NC57-36H-SE
L2Max*
L3Max
MDB Scale
MDB Base
Fixed
NCS-57B1
NCS-57C3
NCS-57C1-48S6H**
NCS-57D2**
Modular
NC57-24DD
NC57-36H6D-S
NC57-MOD-S**
* L2Max/ L2Max-SE planned for XR7.6.1
** Roadmap
Scale Platform can run MDB Base Profile also ( although not required)

## Slide 8: Target Scale Number for MDB profiles
Chart: Unicast Route Scale (in M)
| IPv4 | IPv6
L3MAX | 2.45 | 1.72
L3MAX SE | 5 | 3
L2MAX | 0.3 | 0
L2MAX-SE | 1 | 0.5
Chart: Multicast Route Scale (in K)
| IPv4 | IPv6
L3MAX | 100 | 40
L3MAX SE | 100 | 60
L2MAX | 40 | 20
L2MAX-SE | 50 | 30
Chart: interface Scale
| L3 | L2
L3MAX | 2 | 8
L3MAX SE | 8 | 12
L2MAX | 1.5 | 16
L2MAX-SE | 4 | 16
Chart: BVI/ BD Scale
| Bridge Domain | BVI
L3MAX | 4 | 2.8
L3MAX SE | 8 | 8
L2MAX | 10 | 4
L2MAX-SE | 12 | 10
Chart: L3 & L2 Services Scale
| VRF | L2 PW
L3MAX | 2 | 4
L3MAX SE | 8 | 8
L2MAX | 0.5 | 10
L2MAX-SE | 2 | 12
Chart: L3 & L2 Services Scale
| MAC
L3MAX | 300
L3MAX SE | 500
L2MAX | 600
L2MAX-SE | 650
Target Scale numbers till XR7.7.1 release – Refer 1D sheet for validated scale

## Slide 9: MDB Scale - XR Release Strategy
Enable MDB profile infrastructure including Grid and other enhancements
L3 scale Enhancements
No user configurable MDB profile
Default profiles for Base and SE
7.3.1
L2 Scale enhancements
Support L3Max and L3Max-SE profiles with overall higher scale
Not configurable. Base defaulted to L3Max and SE/eTCAM defaulted to L3Max-SE.
7.4.1
CLI configuration for various profiles – J2/J2C/Q2A/Q2C with MDB profiles.
Support L2Max & L2Max-SE profile configuration J2/J2C/Q2C
7.5.2 & 7.6.1
J2C/Q2C specific enhancements – L3Max and L2Max
L2Max for Q2A
Provide any additional scale enhancements for L2Max and L2Max-SE
7.7.1

## Slide 10: Demo!

## Slide 11: Demo – Commands Used
Fixed
show platform | i RUN
show ver | i "NCS|Version"
Check MDB Profile
show hw-module profile mdb-scale
Check NPU resources
show controllers npu resources lem location all
show controllers npu resources lpm location all
show controllers npu resources exttcamipv4 location all ( for –SE)
Broadcom SDK view of carving
show controllers fia diagshell 0 "mdb info" location all
Modular
show platform | i RUN
show ver | i "NCS|Version"
Check MDB Profile
show hw-module profile mdb-scale
Check if system is in Native mode
show hw-module profile npu-operating-mode
Check NPU resources
show controllers npu resources lem location <>
show controllers npu resources lpm location <>
show controllers npu resources lpm location <>( for –SE)
Broadcom SDK view of carving
show controllers fia diagshell 0 "mdb info" location all

## Slide 12: Resources
NCS 5500 Sharepoint
NCS 5500 Boiler Plate
NCS5500 1D scale
NCS 5500 Deep Dive Deck
@XRDOC
NCS 5500 Sales Connect