## Slide 1: Cisco NCS5500/5700
Akshaya Kumar Sankaran, MIG TME
Nikita Bagaria, MIG PM
9th Feb 2022
Innovation/ J2 MDB Profiles, Use cases
Deepak Balasubramanian, MIG TL

## Slide 2: Cisco Disclaimer
Many of the materials and screen captures described here are highly confidential - the BRCM J2 Pipeline charts etc. The Multi-Dimensional Scale numbers are relevant for the specific use cases only. Please keep this for Cisco internal reference only

## Slide 3: NCS 5500/NCS5700 Innovation
Fill this with a relevant photo, illustration, graph, etc.
NCS 5700 Solution Roadmap
Deployments, Challenges, Solutions - Today
New NCS5700 Enhancements - J2 MDB
NCS5700 Resources Deepdive
Yes, It Works Beyond Slides
Usecases: Peering, Business EVPN

## Slide 4: NCS 5500/5700 Portfolio
Jericho
Jericho+
Jericho2
NCS 5508
NCS 5516
NCS 5504
Jericho2C/
Qumran2C
NC57-36H-SE
NC57-36H6D-S
NC57-24DD
NC57-18DD-SE
4/8/16 J2 Ready FC2 & FAN2
NC55-32T16Q4H-A
NC55-MOD-A-S/SE
NC55-18H18F
NC55-24H12F-SE
NC55-24X100G-SE
NC55-6x200-DWDM-S
NC55-36X100G-A-SE​
NC55-36X100G/-S
Modular
Linecards
NCS 55A1-36H-S/SE
NCS 55A1-24H
NCS-57C3-MOD/SE
NCS 5502/SE
NCS 5501/SE
NCS 55A2-MOD-S/SE/HD/HX
NCS-57B1-6D24/5DSE
NCS-55A1-48Q6H
NCS-55A1-24Q6H-S/SS
Fixed
Jericho2C+
NCS-57C1-48Q6D-S
NCS-57D2-18D
NC57-48Q2D-S/SE*
* Under Consideration
NC57-MOD-S
Notes: NC55-32T16Q4H-A
NC55-MOD-A-S
NC55-MOD-A-SE-S
NC55-18H18F
NC55-24H12F-SE
NC55-24X100G-SE
NC55-6x200-DWDM-S
NC55-36X100G-A-SE
NC55-36X100G/-S
NCS-55A1-36H(-SE)-S
NCS-55A2-MOD-S / HD-S / HX-S
NCS-55A2-MOD-SE-S /-SE-H-S
NCS-55A1-24H
NCS-55A1-24Q6H-S / 24Q6H-SS
NCS-55A1-48Q6H
NCS-5501(-SE)
NCS-5502(-SE)

## Slide 5: NCS 5500/5700 Positioning & Portfolio of Services
IP/MPLS LSR, EVPN/SR, MACsec, IPoDWDM
EVPN/SR-TILFA/TE/ODN
Sticky EMCP
VXLAN DC GW/GPE
Data Center
VPWS, EVPN P2MP, L2/L3 VPN
L2 MCAST, BGP PIC-Edge, mVPN
SRV6
Aggregation
v4/v6 Scale ACL/LPTS/
LI, uRFP, Hybrid ACL, Storm Control
BGP FlowSpec, QPPB
Ingress/Egress Netflow
Peering
IPv4/v6 MPLS, BFD, LSR, MPLS-TE, PIM
TI-LFA, LDPoTE
IPv6 BFD, SRv6
LSR/Core
VPWS, L2/BVI
TWAMP, Y.1732, Eth Loopback, Timing
G.8032, DHCP, GTP Hashing
IP-SLA, Y.1564
SP Access / 5G
L2 MCAST, IGMP Snooping
802.1X, Dual v6 Source, DHCP snooping
MLD Snooping
R-PHY (CIN)
64-Bit Container
IOS-XR
IOS-XR as an App
Common across form factors
Simplified Operations
Boot Time Optimization
Ultra High Density

## Slide 6: NCS 5500/5700 SW Plan in CY22/CY23
XR 75x/761
CY23 SW Release
CY22 SW Release
XR 771
XR 781*
XR 791*
HW/NPI Fixed: Twins Modular: Vigor-Mod
MPA: Bearfoot MPA
New Use cases
ETM, MDB Scale
High Scale Aggregation: L2Max & L2Max-SE profile configuration J2/J2C/Q2C
Critical Customer Escalations
SRV6, BGP MP, Mcast, EVPN, BFD, ACL
J2 Parity
Achieved: 86% J2 Native Parity
Optics, Timing
ZR/ZR+, Class C
L2, L3 and Transport Layer features
HW/NPI
MPA: Private Line Emulation MPA
New Use cases
MDB Scale: High Scale Aggregation J2C/Q2C specific enhancements – L3Max and L2Max
Critical Customer Escalations
EVPN, L2PT,Mcast/MVPN
J2 Parity
Achieved: 87% J2 Native Parity
Optics, Timing 100G-ZR4, ZR/ZR+, Class C
L2, L3 and Transport Layer features
HW/NPI Fixed: Castle Black MPA: Wingbow MPA
New Use cases
PWHE Phase1
J2 Parity
Plan : 92% J2 Native Parity L2, EVPN, Mcast, Forwarding
Optics, Timing
CFP2, QSFP EDFA, Class C
L2, L3 and Transport Layer features
SRV6, SR-OAM
HW/NPI Modular: Vigor-LS
New Use cases
PWHE Phase2, VXLAN DCI
J2 Parity
Plan : 100% J2 Native Parity L2, EVPN, Mcast, Forwarding
Optics, Timing
High power ZRP
L2, L3 and Transport Layer features
SRV6, SRTE,SR:PM
* Release not EC’d yet, planning still in process.
Critical Customer Commitments/Escalations
Critical Customer Commitments/Escalations

## Slide 7: MDB Scale - XR Release Strategy
Enable MDB profile infrastructure including Grid and other enhancements
L3 scale Enhancements
No user configurable MDB profile
Default profiles for Base and SE
7.3.1
L2 Scale enhancements
Support L3Max and L3Max-SE profiles with overall higher scale
Not configurable. Base defaulted to L3Max and SE/eTCAM defaulted to L3Max-SE.
7.4.1
CLI configuration for various profiles – J2/J2C/Q2A/Q2C with MDB profiles.
Support L2Max & L2Max-SE profile configuration J2/J2C/Q2C
7.5.2 & 7.6.1
J2C/Q2C specific enhancements – L3Max and L2Max
L2Max for Q2A, MDB Profiles for J2C+
Provide any additional scale enhancements for L2Max and L2Max-SE
7.7.1/7.8.1

## Slide 8: Deployment with NCS 5500/ NCS 5700

## Slide 9: Services scale requirements
Content Provider
Mobile Packet Core/ Broadband
Private Cloud
Peering /
Direct Connect
Public Cloud
Core
Aggregation
Residential
Business
Mobile
Cable
FTTH
Mobile Backhaul
Metro Ethernet
Aggregation
Business Services
L2 Services – P2P, P2MP (VPWS/VPLS/EVPN)
Higher MAC Table
MPLS services label /SRTE/SRv6
Bridge domain/ BVI
L2 Sub-interface
Aggregation
Mobile Services
L3 Services – VRF, L3VPN
BGP LU
L3 Sub-interface
ARP scale
SRTE/SRv6 PIDs
Core & Peering
LSR & Internet scale
IPv4/ IPv6 L3 Route Table
Multicast route

## Slide 10
NCS-540
N540-24Q8L2DD-SYS
Content Provider
Private Cloud
Peering /
Direct Connect
Public Cloud
NCS5504/08/16
NC57 -SE Line cards
NCS-57B1 -SE
NCS-57C3 -SE
NCS5504/08/16
NC57 Line card
NCS-57B1
NCS-57C3
NCS-57B1
NCS-57C3
NCS-57C1/C3
Core
Aggregation
Pre-Aggregation
NCS 5504/08/16
Modular: up to 9.6T/slot
153.6Tb System
Fixed: Up to 4.8T
NCS 57B1
NCS 57C3
Fixed: Up to 4T
NC57-24DD
NCS57-18DD-SE
NC57-36H-SE
NC57-36H6D-S
NCS-57B1-6D24H
NCS-57B1-5D24H-SE
NCS-57C3-MOD
NCS-57C3-MOD-SE
NCS57C1-48C6-SYS
Residential
Business
Mobile
Cable
FTTH
Mobile Backhaul
Metro Ethernet
High Scale Converged SDN Network
Unique services / scale for different use cases
Next-Gen ASIC
Mobile Packet Core/ Broadband
J2
J2C/
Q2C
L3 Profile
L2 Profile
Q2A
J2C+
NCS540
Access
NCS 540

## Slide 11: NCS 5500 Enhancements Quick review

## Slide 12: ASIC Resource enhancement in J/J+
Jericho
Jericho+
J2
J2c
J2c+
NCS5501
NCS5502
NC55-18H18F
NC55-36X100G
NCS55A2-MOD-S
NCS55A1-24H
NC55-36X100G-A-SE
NC55-MOD-A-S
NCS57B1-6D24H
NC57-24DD
NC57-18DD-SE
NC57-36H6D-S
NC57-36H-SE
NCS57C3-MOD
NCS57D2
57xx for J2/J2c/J2c+
B/C/D for fixed platforms

## Slide 13: ASIC Database resource to Feature/Application mapping
Some commonly known Databases in ASIC
Each database is used for 1 or more use cases /Feature in pipeline.
Feature to database scale not 1:1 mapping.( other parameters also influence scale)
Database | Description | Feature/Application
LPM/ KAPS | Longest Prefix Match or KBP Assisted Prefix Search | IPv4/v6 prefixes
LEM | Large Exact Match Database | IP Host /32, MAC, MPLS
iTCAM | Internal TCAM | ACL
eTCAM | External TCAM on Scaled formfactors (–SE) only | Extended unicast routes, ACL & counters
OEM | OAM Exact Match | OAM Classification
FEC | Forwarding Equivalence Class | Forwarding Information
VSI | Virtual Switch interface | L3 interface, Bridge domains
In-LIF | Ingress Logical Interface table | Logical interface table
EEDB | Egress Encapsulation Database | Tunnel Encapsulation information
GLEM | Global LIF exact Match | Global Id Match

## Slide 14: Enhancements in NCS5500 – J/J+ based platforms
LEM/ LPM
  ( eTCAM) – higher route/ mcast acl etc
EEDB resources
  With SR we have swap labels
ECMP FEC
  Resource optimizations with dlb programming
  LSR & LER – with services ( XR7.1.1, XR7.4.1)
  BGP-LU enhancement – (XR7.5.2)
SRv6 – on J+
All enhancements focuses on how features mapped to fixed set of resources

## Slide 15: NCS 5700 Enhancements

## Slide 16: Transition from NCS5500 (J/J+) to NCS5700 (J2)
L2 Services | NCS5700 (J2/J2C/Q2C) | NCS5500 J/J+
Number of BDs/EVI | 2000 | 1500
ACs per BD | 4K | 512
VPLS PWs (across all BDs) | 4K | 3K
MACs per System | 300K | 128K
L3 Services | NCS5700 (J2/J2C/Q2C) | NCS5500 J/J+
IPv4 Routes | 5M | Upto 4M
IPv6 Routes | 3M | 2M
ECMP-FEC resource | Upto 32K | Upto 4K
Label Stack |  | 
Without recycle | 10 ( 8 Transport + 2 services) | 6 Transport (or) 3 Transport + 2 Service
With recycle | 12 | 12 Transport (or) 9 Transport + 2 Service
All scale values are planned in (1D) Single Dimension
NCS5700 can support
Port Speeds Up to 400G
ASIC SERDES
Header Parser
Support for 50G SerDes in J2/J2C/Q2C
NCS5700 can natively support SRv6 Labels
Support for 144bytes System header (vs 128 bytes in J+)
Transitioning to NCS5700 (J2) is already beneficial given the improvements over NCS5500 (J+)
Top resources/ features improved in NCS5700(J2)

## Slide 17: What's new with J2/J2C/Q2A/Q2C/J2C+
Enhancement on how features mapped to resources
Enhancements on how ASIC resources are carved
MDB
Modular Database

## Slide 18: MDB in J2/ J2C/Q2C/Q2A/J2C+..
MDB : Modular Database
  Instead of dedicated memories
  Different allocation for different profiles
  LEM / LPM-KAPS / FEC / …
Off-chip
Buffers
Fabric Interface
Network Interface
Ingress
Egress
LPM
LEM
TCAM
STAT
FEC
PP
TM
PP
TM
On-chip Buffer
PP
TM
PP
TM
OTM
LPM
LEM
TCAM
STAT
FEC
OP
eTCAM
Fabric Interface
Network Interface
Ingress
Egress
PP
TM
PP
TM
PP
TM
PP
TM
HBM
On-chip Buffer
OTM
OP2
eTCAM
MDB

## Slide 19: MDB: Shared between Cores, Shared between Ingress & Egress paths
Total MDB space is shared by different functions in the pipeline
MDB databases are created at boot time
Database carved for features will increase or decrease based on MDB Profile
Total MDB Space

## Slide 20: MDB Profile resource carving
LEM
LPM
ISEM
L3 Profile
LEM
LPM
ISEM
L2 Profile
Higher or Lower database based on usecase
Total Database is still same
If LPM reduced by X amount, then LEM need not be increased same amount

## Slide 21: MDB Profiles
L2Max-SE*
L3Max-SE
Today we have planned 4 MDB Profiles
Target platforms from XR7.6.1
Fixed
NCS-57B1-SE
NCS-57C3-SE
Modular
NC57-18DD-SE
NC57-36H-SE
L2Max*
L3Max
MDB Scale
MDB Base
Fixed
NCS-57B1
NCS-57C3
NCS-57C1-48S6H**
NCS-57D2**
Modular
NC57-24DD
NC57-36H6D-S
NC57-MOD-S**
* L2Max/ L2Max-SE planned for XR7.6.1
** Roadmap
Scale Platform can run MDB Base Profile also ( although not required)

## Slide 22: Some resources are not modified between MDB Profiles
ECMP-FEC
While FEC changes, ECMP-FEC 32K remains same across all 4 MDB Profiles
VOQ
QoS resources such as VoQ remains same across all 4 Profiles
eTCAM ( only for –SE)
The size of eTCAM would remain same-
But the applications used will vary based on profile
Broadcom MDB Carving allows modifying internal J2 resources
Cisco IOS XR can carve internal resource and also the eTCAM
Some resources are not changed between MDB Profiles
Fixed Resources across 4 MDB profiles
Counters
Counters and Stats resources are fixed for all 4 MDB profiles
MDB Profiles available today
L3Max, L3Max-SE, L2Max, L2Max-SE
Multicast
Multicast DB (for MCID ) will remain same for all 4 MDB profiles

## Slide 23: Platforms with MDB Profile Support
J2
J2C/Q2C
NCS57C3
NCS57C1
J2C+
NCS57D2
NCS57B1
NC57-24DD
NC57-18DD-SE
NC57-36H6D-S
NC57-36H-SE
NC57-MOD
All 4 MDB Profiles will be supported
L3Max/L2Max/L3Max-SE/L2Max-SE
Q2A
NCS540
N540-24Q8L2DD-SYS
J2 Scale
J2C and Q2C MDB internal resources same as J2
Q2A Scale
J2C+ Scale

## Slide 24: MDB scale vs MD scale vs 1D scale
MDB Profile Scale
  Ability to carve same ASIC resources to multiple Profiles based on Use-cases. The scale numbers for each profile are often 1D.
  ASIC
  J2/Q2A/J2C/Q2C/J2C+
  Profiles
  L3Max/L2Max/L3Max-SE/L2Max-SE
Multi-Dimension Scale ( MD scale)
  Refers to feature scale of platform measured with multiple features enabled at same time ( Usually refers to specific customer profiles validated)
One-Dimension Scale ( 1D scale)
  Refers to feature scale of platform measured by configuring single feature only ( Max platform scale for specific Feature)

## Slide 25: MDB profiles Scale comparison Compare between all 4 Profiles on NCS5700
Chart: Unicast Route Scale (in M)
| IPv4 | IPv6
L3MAX | 2.45 | 1.72
L3MAX SE | 5 | 3
L2MAX | 0.3 | 0
L2MAX-SE | 1 | 0.5
Chart: Multicast Route Scale (in K)
| IPv4 | IPv6
L3MAX | 100 | 40
L3MAX SE | 100 | 60
L2MAX | 40 | 20
L2MAX-SE | 50 | 30
Chart: interface Scale (in K)
| L3 | L2
L3MAX | 2 | 8
L3MAX SE | 8 | 12
L2MAX | 1.5 | 16
L2MAX-SE | 4 | 16
Chart: BVI/ BD Scale (in K)
| Bridge Domain | BVI
L3MAX | 4 | 2.8
L3MAX SE | 8 | 8
L2MAX | 10 | 4
L2MAX-SE | 12 | 10
Chart: L3 & L2 Services Scale (in K)
| VRF | L2 PW
L3MAX | 2 | 4
L3MAX SE | 8 | 8
L2MAX | 0.5 | 10
L2MAX-SE | 2 | 12
Chart: MAC addresses (in K)
| MAC
L3MAX | 300
L3MAX SE | 500
L2MAX | 600
L2MAX-SE | 650
Target Scale numbers till XR7.7.1 release – Refer 1D scale for validated scale
Notes: Cisco MDB profile based on Real customer use-cases & more features
- Preferring one profile doesn’t deplete resource for other service completely
( which is Broadcom default design)
(eg) There is basic L2 scale in L3Max and basic L3 scale in L2Max – providing

## Slide 26: Compare NCS5500 (J/J+) to NCS5700 (J2) with MDB
L2 Services | NCS5700 L2Max-SE (J2/J2C/Q2C) | NCS5500 (-SE) J/J+
Number of BDs/EVI | 2000 | 1500
L2 subinterface without BVI/QoS | 16K | 8K
Total PWs (across all BDs) | 12K | 3K
MACs per System | Upto 600K | 128K
BVI | 10K | 1250
L3 Services | NCS5700 L3Max-SE (J2/J2C/Q2C) | NCS5500 (-SE) J/J+
IPv4 Routes | 5M | Upto 4M
IPv6 Routes | 3M | 2M
VRF | 8K | 4K
L3 subinterface without QoS | 8K | 2K
L2 subinterface without BVI/QoS | 12K | 8k
MACs per System | 500K | 128K
BVI | 8K | 1250
All Scale values are 1D scale – some are still in Roadmap
Refer 1D scale sheet for validated scale
Transitioning to NCS5700 (J2) with MDB - NCS5500 (J+)
Top resources/ features improved in NCS5700(J2)

## Slide 27: How to configure MDB NCS5500 Modular platform
  No MDB Profile
J2 Native Mode
Jericho2-SE
Jericho2-SE
Jericho2-SE
Jericho2-SE
Jericho2-SE
Jericho2-SE
Jericho2-SE
Jericho2-SE
System with only J2 cards
Modular Chassis default loads in Compatibility Mode ( even with only J2 cards )
  MDB profile not Supported in
  J/J+ and J2 Compatibility Mode
J2 Compatibility Mode
1
STEP
System Boot up
2
STEP
L3Max
2
STEP
L3Max
Can configure both hw-profiles
Single Reload
Reload required
J2 Comp to J2 Native mode
Jericho
Jericho
Jericho
Jericho+
Jericho2-SE
Jericho2-SE
Jericho2-SE
System with J+ & J2 cards
Jericho2-SE
hw-module profile npu native-mode-enable
hw-module profile mdb l3max-se
Reload required
L3Max to L3Max-SE
System with only J2 cards
J2 Native by default loads with L3Max MDB Profile
When Chassis has only –SE card MDB L3Max-SE can be configured
J2 Native Mode
Configure hw-module for Native mode after remove J/J+ Line cards.
J2 Comp
vs
J2 Native
MDB Profile
hw-module profile npu native-mode-enable
hw-module profile mdb l3max-se
  L3Max
  L3Max-SE

## Slide 28: MDB Profiles : Cisco vs Other Vendors
7800R3K Series | 7800R3K Series
Profile | L3-XXXL Profile
MAC Addresses | 384K
NCS5700 carving has validated profiles for L3 and L2
Arista 7800R3K Series |  |  | 
L3-XL Profile (default) | L3-XXL Profile | L3-XXXL Profile | Balanced-XL Profile
NCS5700 –SE ( Scale) | 7800R3K Series
Profile | L3Max-SE & L2Max-SE
MAC Addresses | 500K
Cisco NCS5700 ( -SE) |  |  | 
L3Max-SE | L3Max | L2Max | L2Max-SE
Note: All 4 MDB Profiles supports all features only scale will change
1D Scale published by any Vendor is not usually real
But we validated higher scale because of our MDB approach (ex: MAC scale)

## Slide 29: MDB Profile Configuration/ Verification
Configure MDB Profile
“hw-module profile mdb <l3max | l3max-se | l2max | l2max-se>
Verify MDB Profile
Check MDB Profile
show hw-module profile mdb-scale
Broadcom SDK view of carving
show controllers fia diagshell 0 "mdb info" location all
Verify J2 Native mode - Only for Modular (NCS5504/08/16)
show hw-module profile npu-operating-mode
Verify Resource Utilization
Check NPU resources
show controllers npu resources lem location all
show controllers npu resources lpm location all
show controllers npu resources exttcamipv4 location all ( for –SE)
Configure Native Mode
hw-module profile npu native-mode-enable
Notes: Planned and carved 4 MDB profiles for J2 family.
MDB profile carving, loading and Grid Infra ready for all platforms based on J2/J2C/Q2A and Q2C.
Same command applies for all platform/ASIC types. System internally maps the profiles to platform and line card types.
Default profiles for all platforms automatically loaded and does not require config.
show command will be added to display the currently active MDB profile (7.5.2 onwards)

## Slide 30: Deployment with J2 MDB

## Slide 31: How MDB Profile works in Modular NCS5500 + NC57 Line card
System Scale : L3Max
LC0: L3Max
User Input
CLI or Default Profile
hw-module profile mdb <l3max|l2max>
Base
Linecard
LC1: L3Max
LC2: L3Max
Scale
Linecard
LC3: L3Max
Scale
Linecard
Scale
Linecard
System Scale : L3Max-SE
hw-module profile mdb <l3max-se|l2max-se>
No
Linecard
LC1: L3Max-SE
LC2: L3Max-SE
Scale
Linecard
LC3: L3Max-SE
Scale
Linecard
Scale
Linecard
NCS5504 Mix Base and Scale Linecards
Only Base MDB Profiles supported
NCS5504 Only Scale Linecards
All MDB Profiles supported
Slot 0 : Base J2 Linecard
Slot 1-3: Scale J2 Line cards
Slot 0 : Remove Base LC
Slot 1-3: Scale J2 Line cards
Base MDB Profiles supported
Enhanced MDB Profiles supported*
RP
Scale Profile
LC NPU
ASIC MDB setting
LC NPU :
Scale line card –SE profile will always have SE profile, even if L3Max is configured at RP.
Scale is determined by Scale profile Globally in RP.
RP :
System-level profile in RP determines scale
Remove Base LC and reload –
hw-module config admin reload rack 0
Notes: “hw-module profile mdb <l3max | l3max-se | l2max | l2max-se>
Planned and carved 4 MDB profiles for J2 family.
MDB profile carving, loading and Grid Infra ready for all platforms based on J2/J2C/Q2A and Q2C.
Same command applies for all platform/ASIC types. System internally maps the profiles to platform and line card types.
Default profiles for all platforms automatically loaded and does not require config.
show command will be added to display the currently active MDB profile (7.5.2 onwards)
  show hw-module profile mdb-scale

## Slide 32: How MDB Profile works in Fixed NCS5700, NCS540 (N540-24Q8L2DD-SYS)​​​​
System Scale : L3Max
NPU0: L3Max
User Input
CLI or Default Profile
hw-module profile mdb <l3max|l2max>
System Scale : L3Max-SE
hw-module profile mdb <l3max-se|l2max-se>
NPU0: L3Max-SE
Fixed Base Platform
J2/J2C/Q2A/Q2C/J2C+
Base MDB Profiles supported
Enhanced Profiles supported
RP
Scale Profile
LC NPU
ASIC MDB setting
Fixed Scale Platform
J2/J2C
Notes: “hw-module profile mdb <l3max | l3max-se | l2max | l2max-se>
Planned and carved 4 MDB profiles for J2 family.
MDB profile carving, loading and Grid Infra ready for all platforms based on J2/J2C/Q2A and Q2C.
Same command applies for all platform/ASIC types. System internally maps the profiles to platform and line card types.
Default profiles for all platforms automatically loaded and does not require config.
show command will be added to display the currently active MDB profile (7.5.2 onwards)
  show hw-module profile mdb-scale

## Slide 33: Understanding Resource carving
“hw-mod mdb profile”
  used to set the “system profile” & control the system scale
  MDB resources carved based on the LC profile
MDB
[On-Chip Resource]
  LEM DB
  Labels, l2 BRMAC, host routes*
External TCAM
[SE LC/ Systems ]
  KBP_TCAM_FWD DBs
Internal TCAM
[On-Chip- no static carving]
  QoS
  I/f, Tunnel & OAM DBs
  EEDB Cluster banks
  Indirection pointer for GLIF & label Instructions
  ECMP_FEC
  Outlif tables for LABELS, ARP ..
  V4, V6 Unicast prefixes,
  Multicast routes,
  RPF DB
  Ext_FG DBs
  v4,v6 Flowspec (SE only),
  v4,v6 LPTS(75x Rls)
  v4,v6 Ingress ACL (inc chained ACL)
  Stats –
  OAM DBs- CFM/BFD
  ACL
  LI
  Stats
  All Flow-Group & Stats DBs*
  InLif, VSI,ISEM, ESEM..
  QoS, VoQ, l3/l2 Rx/TX
  Egress, Hybrid ACL
  ACL, FS, MPLS, LPTS etc
  LPM KAPS DB
  v4,v6 Unicast prefixes*, Multicast routes*
  FEC Hierarchies
* For Base LC

## Slide 34: NCS5700 - 3 Level FEC Hierarchy
H1 FEC
H2 FEC
H3 FEC
H1 ECMP
H2 ECMP
H2 ECMP
ECMP-FEC
Hierarchy 1
Hierarchy 2
Hierarchy 3
Total 32K Entries
16 Banks (each 2K entries)
Every Bank to 1 Hierarchy only
IGP Routes, BGP-LU Interface Peering, SRTE, Multicast, L2Sub
  BGP-LU Loopback Peering, Recursive MPLS routes, VPN over IGP MPLS, RSVP-TE Mid-Point Protection., SRv6 DT4/DT6/DX2, L2vpnPW
VPN/EVPN over BGP-LU Loopback Peering
FEC carving at Init Time based on MDB
3 Level of Hierarchy of H1, H2, H3 in FEC & ECMP FEC
Different ranges for each Hierarchy
FEC
16 Banks
ECMP FEC
FEC
Applications
FEC usage per hierarchy | show controllers npu resources fec location 0/0/CPU0 | Note: OOR is per FEC hierarchy ​
ECMP FEC usage per hierarchy | show controllers npu resources ecmpfec location 0/0/CPU0 | Note: OOR is based on total ECMP FEC consumption (NOT per hierarchy)​

## Slide 35: NCS5700 Encapsulation in EEDB
EEDB management in NCS5700(J2) uses Logical_phase - (represented by the - 1,2,3.. 8)
Logical_phase maps to Physical phase - (represented by the size - XL/L1/M1/S1 ..etc)
Cluster Bank Pair : EEDB_S2_XL Cluster S2 and XL combined
Max-Entries : 98304 /*S2 and XL combined MAX entries, fixed*/
Total In-use : 0 /* S2 and XL combined in use*/
Start of second block XL in bank pair S2_XL
Logical_phase : 1 (Encap_Rif) /*Logical phase 1 /feature map: Encap Rif for this bank block*/
Cluster Bank
Bank Size : S2 /*This is S2 cluster bank*/
Estimated Max Entries : 98304 /*Dynamic calc estimated max entries for S2*/
OOR State : Green /*OOR state for S2/ Phase 1*/
Total In-Use : 0 /*Total used entries for phase 1*/
EEDB Bank: /*Start of LL banks for S2 block*/
Estimated Max Entries : 8192 /*Dynamic calc estimated max entries for LL bank*/
OOR State : Green /*State of LL bank*/
Total In-Use : 0 /*Entries used in LL bank of S2 block*/
Start of second block XL in bank pair S2_XL
Logical_phase : 6 (Tunnel4) /*Logical phase: 6 /feature map: Tunnel4 for this bank block*/
Cluster Bank
Bank Size : XL /*This is XL cluster bank*/
Estimated Max Entries : 73728 /*Dynamic calc estimated max entries for XL*/
OOR State : Green /*OOR state for XL block*/
Total In-Use : 0
EEDB Bank: /*Start of LL banks for XL block*/
Estimated Max Entries : 63488 /*Dynamic calc estimated max entries for XL block*/
OOR State : Green /*State of LL bank*/
Total In-Use : 0 /*Entries used in LL bank of XL bl
Output : show controller npu resources encap
Understanding EEDB bank pairs and usage

## Slide 36: EEDB phase Map
Cluster Bank Pair | Physical Phase (size) | Logical Phases (from L2MAX) | Applications
EEDB_S2_XL | S2 | Logical_phase : 1 (Encap_Rif) | RIF, SRv6 H.Encap
 | XL | Logical_phase : 6 (Tunnel4) | IGP, BGP-LU interface peering, SRTE(1,2 label), SRv6 T.Insert
EEDB_L2_M3 | L2 | Logical_phase : 2 (Encap_NativeArp) | VPN/EVPN/SRTE(9,10 label), SRv6 T.Insert
 | M3 | Logical_phase : 8 (Encap_Ac) | AC Outlif, Non-VRF ND
EEDB_M1_M2 | M1 | Logical_phase : 3 (Encap_NativeAc or Tunnel1) | BGP-LU Loopback peering, SRTE(7,8 label), SRv6 T.Insert
 | M2 | Logical_phase : 5 (Tunnel3) | SRTE(3,4 label), SRv6 T.Insert
EEDB_S1_L1 | S1 | Logical_phase : 4 (Encap_Tunnel2) | SRTE(5,6 label), SRv6 T.Insert
 | L1 | Logical_phase : 7 (Encap_Arp) | ARP, ND, SRv6 H.Encap
Bank Pair to phase map changes based on configured MDB profile
Note
EEDB carving Specific to L2MAX MDB profile

## Slide 37: NCS5700 Deployments Use case #1 Peering L3 Services
L3Max-SE
7.5.1
MDB Profile
IOS XR

## Slide 38: Peering Network Requirements L3 Internet Edge
Peering Profile with Higher route scale,
  Internet route scale
  IPv4 : Upto 1M ( with uRPF)
  IPv6 : Upto 200K ( with uRPF)
Security Focus
  BGP FlowSpec
  ACL
  uRPF
High density peering interfaces – 8K
Routing Control Plane
  20% BGP
  80% static
Use Case | Peering
Line Cards | J2-SE
MDB Profile | L3Max-SE
Peer 1
Peer 2
Transit
SP Network
High Scale Peering

## Slide 39: Peering - Network Requirement Summary
Use Case | Peering L3 Services
Line Cards | J2-SE
MDB Profile | L3Max-SE
High Scale Peering specific Requirements | 
ACL Entries ( v4/ v6) | 37000
BGP Flowspec | 20K
BGP Peers | 2400
Interfaces Logical L2/L3 | 8000
ECMP Groups | 32K
Routing Scale | 
IPv4 UC routes - per system (uRPF) | 1.4M
IPv6 UC routes - per system (uRPF) | 200K
MPLS Labelled routes (BGP-LU) IPv4/v6 ( single-path) | 50K
VRF Instances | 5
Static IPv4 / IPv6 routes | 50K /20K

## Slide 40: Route Scale
L3 Interfaces | 8000
IPv4 ( Global/VRF) (uRPF) | 1.3M/ 100K
IPv6 ( Global/ VRF) (uRPF) | 300K/ 100K
BGP Peers | 2400

## Slide 41: Security – ACL, BGP-Flowspec
ACL Entries | 37930
BGP Flowspec | 20804

## Slide 42: Route scale – Transport IPv4/v6/ BGP LU Resources
IPv4 Route | 1.4M
IPv6 route | 443371
BGP-LU (MPLS Label) | 31000
MPLS Label: BGP-Labelled Unicast
IPv4 Routes
IPv6 Routes

## Slide 43: Egress Encapsulation stored - EEDB
Encapsulation for Outgoing packets
EEDB Logical Phases
Encapsulation Database has upto 8 Phases
Each phase can be used by different applications and internally mapped to MDB resources
Resources Mapped will vary based on Profile
IPv4 Next Hop (ARP) | 1616
IPv6 Next Hop (ND) | 1115
MPLS ( Labelled/BGP-LU ) | 62057

## Slide 44: NCS5700 Deployments Use case #2 Business L2 Services
L3Max-SE
7.5.1
MDB Profile
IOS XR

## Slide 45: Business L2 Services
L2 Services - Point to Point, Point to Multi-Point ; BGP - L2VPN(EVPN)
Core
Business
Connectivity
NCS 5700
(Agg)
BGP-LU
BGP-LU
BGP-LU
Business &
Residential
Connectivity
CABLE
Transport : iBGP LU / Static route
NCS5700 is Aggregation node for L2 Services
Old Network based on L2VPN VPLS/ VPWS
Port and VLAN Based L2 Services
BGP EVPN
  EVPN-VPWS (Point to Point)
  EVPN-VPLS (Point to Multi-point)
  Single Port-active ( Active/Standby) LAG (2x100G)
EVPN control plane based for MAC learning over core
Use Case | Business L2 Services
Line Cards | J2-SE
MDB Profile | L3Max-SE
NCS 5700
(Agg)
EV-LAG
MH - Single Port-Active
EV-LAG
MH Single Port-Active

## Slide 46: Business L2 Services Network Requirement Summary
Use Case | Business L2 Services
Line Cards | J2-SE
MDB Profile | L3Max-SE
High Scale Peering specific Requirements | 
MAC Address | 500K
MAC Address per VSI | 1000
Interfaces Logical L2/L3 | 8000
ECMP Groups | 32K
BGP Policies / community list/ RT/RD | 5K
Services Scale | 
EVPN P2P instances | 8K
EVPN MP2MP | 8K
Global IPv4/v6 Routes | 100K
MPLS Labelled routes (BGP-LU) IPv4/v6 | 50K
VRF Instances | 50
CFM MEP ( Local, remote) | 8K

## Slide 47: L2 Services Scale – 500K MAC
500K MAC Scale
500K MAC Programmed in LEM
L2 Services Scale | 1.4M
MAC Scale | 499,999

## Slide 48: L2 Services Scale - Interfaces
L2 Interfaces
CFM MEP
L2 Services Scale | 1.4M
L2 Interface | 8000
CFM MEP | 7000

## Slide 49: L2 Services Scale - EVPN
L2 EVPN
L2 Services Scale | 1.4M
EVPN P2P -VPWS | 8000
EVPN MP2MP -VPLS | 7000
Notes: Future enhancements for resources

## Slide 50: L3 URPF Route Scale - eTCAM
L3 URPF Route
L3 Route Scale | 1.4M
IPv4 URPF Route | 500K
L3 eTCAM Entry
Note : requirement was 100K only

## Slide 51: Sales Resources

## Slide 52: Sales Resources on Sharepoint
SharePoint NCS-5500/5700 top level
https://cisco.sharepoint.com/sites/MIGRoutingPMTMECommunications/SitePages/NCS5500/NCS-5500-Routers.aspx
Link to NCS5500 Sharepoint

## Slide 53: Boilerplate on SharePoint
Link to Boilerplate
https://cisco.sharepoint.com/sites/MIGRoutingPMTMECommunications/SitePages/NCS5500/NCS-5500-Routers.aspx

## Slide 54: 1D Scale sheet on Sharepoint
Link to 1D Scale Sheet
https://cisco.sharepoint.com/:x:/s/MIGRoutingPMTMECommunications/EbHpIe84bF1MrXf3sIRF11gBx-nTEGXpGC_0FHfaR4_wtg?e=bbhwMe

## Slide 56: Competitive - Crowdsourcing activity
Inviting you to join !!!
What … Simple way to combine our knowledgebase on competition
How … if you learn something new about Vendor J/N/A/H
> Directly update your inputs in new slide
> or drop us an email
fretta-tme@cisco.com
Competitive Collateral

## Slide 57: NCS-57C3 default MDB Profile is L3Max
NCS57C3 (Base) and NCS57C3–SE (Scale ) by default loads with L3Max MDB Profile
Reminder
All Modular chassis NCS5504, NCS5508, NCS5512
  Runs eXR
  In J2 Native mode default profile is L3Max (even with J2-SE)
  NCS-57C3
  Consider NCS-57C3 as 3RU Modular
  NCS-57C3 also runs eXR image
  Will load L3Max by default

## Slide 58: Forwarding Paths programmed - FEC
Forwarding Paths
FEC- Hierarchy 3
J2 has 3 Level FEC hierarchy
H3 -> Bottom of Hierarchy for non-recursive paths
Total FEC | 115250
Non-Recursive ( Transport) | 114767