## Slide 1: iNex for Pro’s
How to use
How does it work
How to interpret the various outputs
Tips and Tricks
Hans van Sluis and Gary.E Sachs
18-Dec-2015

## Slide 2: This presentation is based on iNex V1.23-0

## Slide 3: Topics to be discussed (1/2)
Quick Introduction to what iNex is and is not.
Overview of the Graphical User Interface
iNex processing, an in-depth explanation
    Capture and Analysis definitions
    Break-out routines.
Spreadsheet:
    List of available worksheets, including mapping of InSplore data onto spreadsheets.
    Available Macro’s.
    Overview worksheet: System Overview, Health Check Overview, Object Distribution, Analysis Summary.
    Capture worksheets (Captured Log Data Summary, Captured Log Data).
    PD related worksheets (Physical Disks, PD Capacity Charts, PD AscAscq, PD Chunklets).
    Host related worksheets (SAN Ports, Hosts & LUNs, Host Events Summary, Host Events List).
    SR and AO worksheets (SR AO Config and Events, SR AO Logs, SR AO Data Statistics).
    VV related worksheets (Virtual Volumes, RemoteCopy).
    FC and SAS related worksheets (Port x – y, Cage Data, Cage Comms, Port_N_S_P_SAS_PEL, Port_N_S_P_LESB).
    Miscellaneous worksheets (Memory, Tasks, Nodes, Cluster, Index).

## Slide 4: Topics to be discussed (2/2)
auto_update, how does it really (not) works
3PAR Virtualization Mapping Information, the MS-Access database
    Which info is (not) in the database.
    Forms
    Find (and fix) remote chunklets
Customer Found Issue (CFI) database inter-action
    Automatic Upload of GR8/SI case number to CFI.
    Automatic Download of 3PAR oriented copy of central CFI database
    Using MS-Excel to review local copy of CFI database.
    Node Crash Footprint Recognition.
Questions

## Slide 5: Quick Introduction

## Slide 6: Quick Introduction
Gary’s poetry (short version)
iNex is a tool that parses a 3PAR InSplore file, hence the name INsplore Explorer. iNex has both a GUI and CLI interface. iNex also runs on both Windows and Linux. (it also accepts config.<date>.<time>.0001 and evtlog.<date>.<time>.debug files as available on STaTS)
iNex provides a myriad of information regarding configurations with respects to almost every aspect of a 3PAR array… hosts, ports, PDs, LDs, VVs, VLUNs, CPGs, etc. It cross references related information into tables with links for ease of access and review. It provides analysis of the configurations and presents mis-configurations in color coded trees for quick identification. iNex looks at PDs and for SSDs provide a graphical view of how much service life is left. It analyzes AO data. The list goes on…
iNex has a simple but thorough rule set for reviewing the logs and reporting known issues, again presenting this information in color coded trees for quick identification and reference. The rule set is enhanced as an ongoing activity due to knowledge gained while working ERT cases.
iNex also now has the capability to identify when an array is exhibiting issues related to a specific CFI and then post the case number to the CFI automatically!
The next version of iNex is intended to have the capability to do crash dump analysis by looking for known crash footprints and presenting those to the user… quick identification of the crash and if it is known, so is a CFI / bug-number, may be even a fix! That should help reduce AOD and the number of ERT elevations.
iNex creates several MS-Excel spreadsheets to present its findings to the user. The spreadsheets also contains the configuration information in tabular form, with links as previously mentioned, to present the data in an easy and quick navigable format! The spreadsheets also contain graphs where appropriate to help understand the data being presented. iNex also creates an MS-Access database containing PD, LD and VV information that can quickly identify what PD affects what LDs or VVs or both for example. This data also includes the PD chunklets and the LD chunklets. With this kind of data available, quick identification of so called “disk” related problems becomes fast and accurate!
Unfortunately a quick summary will not do iNex the justice it deserves or describe all the great things it can do quickly, efficiently and accurately. Not to mention the time it will save in getting an analysis done and/or identifying problems.

## Slide 7: Quick Introduction
More serious note
iNex is often used in combination with other, Unix-style, tools.
    A deep dive into a complex issue can be more efficient using Unix-style tools (awk / grep / cat / vi ) than Microsoft Excel filter options.
    Typical support environment is Windows based workstation with Virtualized Unix environment:
      MobaXterm
      Vmware Workstation / Oracle VirtualBox with Linux VM in combination with shared access to Windows directories.
iNex contains, uses and produces “HP Internal Information”, like CFI’s, suspect serial number ranges, etc. Therefore, iNex is “HP Internal Use Only”, just like this presentation.

## Slide 8: Overview of the Graphical User Interface

## Slide 9: iNex User Interfaces
Introduction
iNex uses 2 Graphical User Interfaces:
A Graphical User Interface for ‘data processing’.
    This is known as the ‘iNex GUI’.
    Offers a wide range of options for data processing.
    Output will be in the form of Microsoft Excel spreadsheets and / or CSV files.
The User Interface provided by Microsoft Excel:
    Used during data review and data analysis phases.
iNex also supplies a Command Line Interface for ‘data processing‘

## Slide 10: Graphical User Interface 1/5
Version Number,
Patch Number,
Release date
Bitness of iNex
Expiration date
Information on how
iNex is configured
to process the data
As well as installation
info
Notes: The version number is fixed for a specific release.
The patch number is updated if a patch is installed. V1.22-0 indicates that this is V1.22 without any patches. Note that the patch number will be updated (from V1.22 onwards) even if the main executable is not updated.
The bitness of iNex is either 32-bit or 64-bit. During installation time, the user creates a short-cut on the Desktop pointing to the GUI executable. During start-up time, iNex verifies if the bitness of the application (32/64 bit) matches the bitness of the Operating System and will adjust the short-cut accordingly.
The expiration date is always 180 days after the release date. At 00:00:00 of that day, iNex will stop functioning, which the exception of checking for updates. This to avoid that a) users continue to use old versions and b) as this tool is HP Internal Only we want to limit the usage outside HP.
Status Information (most important keywords):
Home Directory : This is the directory in which iNex is installed.
Verify upon installation.
Customers Location : This specifies the directory tree where the data related
to customer cases can be found. Note that the tool
expects the following structure:
<CustomersDirectory>\<Customer Name>\<Case Number>\<Date>
It uses the Customer Location to automatically find and
fill in the customer name and OPT / GR8 /SI number.
Operation Mode : Indicates if iNex will decompress the InSplore or not.
Decompression Method : Indicates if an external decompression program is used
or if the internal method is used.

## Slide 11: Graphical User Interface 2/5
Data processing options are only enabled after a compressed InSplore is dragged and dropped in the GUI
Case Number and
Customer Name
automatically filled in
Note the directory
structure
Notes: NOTE: Only 1 (decompressed) InSplore per directory
Processing Options:
If the InSplore is already decompressed, enable “Input already decompressed”, meaning iNex will find the decompressed InSplore directory and process it.
The mapping information is per default processed. Can be disabled, but then no MS-Access database.
iNex supports 2 output formats, being a spreadsheet (can be read by both OpenOffice on Linux as well as MS-Excel) and CSV files. The latter can be easily (automatically) uploaded into a relational database. During normal processing, both formats should be generated.
The maximum number of events to be processed is limited to 200,000 (32-bit version) or 1,000,000 (64-bit version). The number of events to process is an important factor in both memory usage as well as processing time.
If the spreadsheet containing the configuration information needs to be shared with a customer, enable “Customer Viewable”. Specific HP internal information is then not outputted.
In case the internal decompression methods needs to be used (for example, the external decompression one [7-zip] is not available), enable “Use Internal Decomp Method”.
The “Capture /var/log/tpd & Merge” allows all files in the /var/log/tpd directory of all nodes to be processed and merged in a time-sequence order. Must be used with caution to the massive amount of data which will be generated if not in combination with “Date Time Selection” to specify start date&time and end date&time.
Per default, 7 days (7 * 24 hours, calculated from the time the InSplore was created) backwards will be processed. It is possible to limit the time period by using one of the 2 options:
  “Log Monitor Window”, which allows the reduction / increase of 24 hours periods.
  “Date Time Selection”, which allows the specification of the start date and time as well as the end date and time. Typically used in combination with “Capture /var/log/tpd & merge”
Case number recognition algorithm:
String of 10 digits  GCSS / OPT case number
String of 8 digitis starting with “4000”  GR8 case number
String of “SIE” / “SIA” followed by 5 digits  SIE case number

## Slide 12: Graphical User Interface 3/5
Progress bar and
steps processed / total
List of generated
spreadsheets:
*.main.xlsm,
Use “Open” button to view selected file.
Time stamped
processing and progress
Information. Lists files currently being processed.
Notes: Per default, the output directory is the same as the input directory.
The default selected spreadsheet is the “*.main.xlsm” spreadsheet, so this one will be opened when the “Open” button is selected.
There is no need to leave the GUI if another InSplore needs to be processed. Just press “Clear All”.
In this state, memory is still allocated by the Operating System to iNex. In order to release memory, use “Clear All” or quit the application.

## Slide 13: Graphical User Interface 4/5
Working with config.*.0001 and evtlog.*.debug files from STaTS
Drag and drop directory into iNex
Best practice is to have 1 config file and
multiple evtlog files in the directory.
NOTE: If the directory contains filenames containing the string “aomoves” or “iodensity”, those files will be processed as well
Notes: NOTE: iNex created a dummy, decompressed, InSplore first based upon the information in the config.*.001 and evtlog.*.debug files. This temporary InSplore is created in the temp directory under the home directory of iNex. The temporary InSplore is removed at the end of processing when using the GUI, in case of the CLI the temporary InSplore is not removed.
In case of working with system outages, the evtlog files, especially the non-event information, may need to be edited to allow a smooth processing. In those cases, delete the “showsys –d” output, especially in case of sysmgr not being fully started.

## Slide 14: Graphical User Interface 5/5
Registration of iNex version
From V1.22-1 onward, iNex invites users to register
See picture for registration options.
Will send email to “iNex Support” (inex.support@hp.com)
Requires access to HP Intranet
Notes: Note: Bitness specifies the bitness of the iNex application, not of the OS !!

## Slide 15: iNex processing an in-depth explanation

## Slide 16: iNex processing, an in-depth explanation
iNex processing takes several phases:
    Phase1: Validate the integrity of the data presented to iNex.
      Filename format needs to match specific criteria.
      For InSplores: specific files need to be present.
    Phase2: Process the pre-defined sets of data.
      Defined in internal iNex table, release dependent
    Phase3: Process the files specified in the capture definitions
      Capture definitions are external files, can be changed on demand.
      Unix “grep” style pattern search for specific strings in specified files
    Phase4: Analyze the configuration, event and captured data
      Using built-in analysis routines per object (Events, PD, LD, VV, RCGroup, CPG, etc)
      Using external, Perl, scripts to check for specific configuration issues, possibly related to CFI’s
    Phase5: Generate output
Notes: File Format criteria:
Insplore.140702.113513.26398966
Insplore.140702.113513.26398966.tbz2
Insplore.3PAR-ING-A1-1302606.20130508.1312
Insplore.os-f200-d1-in.cis.tamu.edu-1314405.20130702.1812
Insplore_20140728_172936_CZ33179729.tbz2
Insplore_SDC_20140729_150742.tbz2
evtlog.140618.012345.debug
evtlog_140618_012345_debug
config.140618.012345.debug
config_140618_012345_debug
*aomoves*
*iodensity*
InSplore integrity is verified and decompressed InSplore needs to meet all below criteria:
“showsys.out” file must be present.
“*.node<digit>.*” directory must be present and all have the same date and time.
“Insplor_log.<arrayname>” must be present
<arrayname> must be present in directory containing decompressed Insplore
Appropriate error messages will be generated if one of the above criteria is not met. In that case, the Insplore will not be processed.
InSplore integrity is verified and decompressed InSplore needs to meet all below criteria:
“showsys.out” file must be present.
“*.node<digit>.*” directory must be present and all have the same date and time.
“Insplor_log.<arrayname>” must be present
<arrayname> must be present in directory containing decompressed Insplore
Appropriate error messages will be generated if one of the above criteria is not met. In that case, the Insplore will not be processed.

## Slide 17: iNex processing, an in-depth explanation
Phase2: Processing the iNex internal list
The internal list contains 120+ file- or directory names to be processed.
    The processing of each file is logged in the <INEX_HOME>\log\inex.log file.
    Each file / directory to be processed is linked to a dedicated parsing routine.
    All information, except events, is stored in memory. The larger portion of event information is stored on disk.
  Event information is sanitized towards the end of phase2.
    iNex adds several fields to the event information to facilitate easier sorting later on.
    Dedicated fields for “Port” and “Affected Node”
    Translation of object names in event info into object type and ID’s in dedicated fields
  Specific type of events are internally tracked for grouping / analysis purposes.
Notes: <INEX_HOME>\log\inex.log sniplet
15-Aug-2014:09:18:41 3 Directory "D:\Products\3Par\Perl\Inex\tmp\1438350\InSplore.1438350-" contains 134 files
15-Aug-2014:09:18:41 3 Stat of file "D:\Products\3Par\Perl\Inex\tmp\1438350\InSplore.1438350-/InSplor_log.1438350"
15-Aug-2014:09:18:41 3 Processing events which occured between 22-Jul-2014 08:51:03 and 16-Aug-2014 07:18:37
15-Aug-2014:09:18:41 3 File "showsys_-d.out" opened for READONLY
15-Aug-2014:09:18:41 3 File "showsys_-d.out" closed
15-Aug-2014:09:18:42 3 --> System Name: "US02A0200010001". Type: InServ V800. SN: 1438350
15-Aug-2014:09:18:42 3 --> Nodes: Configured: 4 Online: 0,1,4,5 Participate: 0,1,4,5
15-Aug-2014:09:18:42 1 File "showversion_-b.out" not present in InSplore
15-Aug-2014:09:18:42 3 File "showversion.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showversion.out" closed
15-Aug-2014:09:18:42 1 File "showversion_-a.out" not present in InSplore
15-Aug-2014:09:18:42 3 file "showld.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showld.out" closed
15-Aug-2014:09:18:42 3 file "showvv.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showvv.out" closed
15-Aug-2014:09:18:42 3 File "showdate.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showdate.out" closed
15-Aug-2014:09:18:42 3 file "showpd_-i.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showpd_-i.out" closed
15-Aug-2014:09:18:42 3 file "showcpg_-r.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showcpg_-r.out" closed
15-Aug-2014:09:18:42 3 file "showvvset.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showvvset.out" closed
15-Aug-2014:09:18:42 3 file "showcage_-d.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showcage_-d.out" closed
15-Aug-2014:09:18:42 1 File "showtask.out" not present in InSplore
15-Aug-2014:09:18:42 1 File "showhost_-verbose.out" not present in InSplore
15-Aug-2014:09:18:42 3 file "showport.out" opened for READONLY
15-Aug-2014:09:18:42 3 File "showport.out" closed

## Slide 18: iNex processing, an in-depth explanation
Phase3: Capture and analysis definitions
Capture definitions contain a list of searchable patterns in files.
    If a match is found, the full filename, line number and string will be noted and be part of the output
    Possibility to alert the user of this occurrence by adding an analysis code to the string
    Capture definitions are read during iNex startup.
    Filename: <INEX_HOME>\defs\capture_definitions.txt
    The <INEX_HOME>\defs\capture_all_defs.txt is only used during “Capture /var/log/tpd & merge”.
Analysis definitions contain a list of analysis codes used by several iNex components (internal analysis routines, break-out routines, capture definitions)
    Analysis definitions are read during runtime when needed.
    Filename: <INEX_HOME>\defs\analysis_definitions.txt
Encountered analysis codes are presented on the “Overview” worksheet of the “.main.xlsm” spreadsheet.

## Slide 19: iNex processing, an in-depth explanation
Phase3: Capture and analysis definitions
Example of a capture definitions file
# Search for strings in /var/log/syslog files for all nodes
\S+.node\d+.\S+/var/log/syslog.\d+ ---- info CM Error:
\S+.node\d+.\S+/var/log/syslog ---- info CM Error:
\S+.node\d+.\S+/var/log/syslog.\d+ 1000 warning Linux version
\S+.node\d+.\S+/var/log/syslog 1000 warning Linux version
\S+.node\d+.\S+/var/log/syslog.\d+ 1001 warning CM: unable to join cluster
\S+.node\d+.\S+/var/log/syslog 1001 warning CM: unable to join cluster
Example of an analysis definitions file
1000 Warning Node %p1% reboot observed at %p3%.
1001 Warning Node %p1% is unable to join the cluster.
1002 Error Node %p1% has flusher speed set incorrectly. Use command "/usr/games# cli setmemval …
1003 Warning Node %p1% went through a 'setsysmgr -force_iderecovery'
1004 Warning Node %p1% reports that Slab memory exceeded the Minor boundaries %p2% number of times.
1005 Warning Node %p1% reports that Slab memory exceeded the Major boundaries %p2% number of times.
1006 Warning Port %p1% is not a valid port type. Observed type: %p2%.
Notes: \S+.node\d+.\S+/var/log/syslog.\d+ means:
All /var/log/syslog.<number> files in all node directories
The %p<number>% is filled in at runtime.

## Slide 20: iNex processing, an in-depth explanation
Phase4: Break-Out routines
From V1.21 onwards, iNex supports Perl-based break-out routines.
Main purpose is verification for known configuration issues, possibly related to CFI’s.
  Located in the <INEX_HOME>\defs\cfganal directory
  There is a break-out routine per object:
  Cage, Cluster, CPG, Host, LD, Node, PD, Port, Rcopy, Task, VV
  Also a break-out routine exists for Captured Data and Events.
Notes: #!/usr/bin/perl
#
# Copyright Hewlett Packard 2012 - 2014
#
# version = 1.20
# This script analyzes configuration related issues for vvs.
#
use strict;
use warnings;
# Read in input values
my $common = $ARGV[0]; # iNex_common object
my $type = $ARGV[1]; # Type of configuration objects
my $ptr = $ARGV[2]; # Hash of configuration objects of type $ARGV[1]
my $syssn = $ARGV[3]; # Serial Number of the system
my $model = $ARGV[4]; # Model of the system (F200, V400, etc)
my $version = $ARGV[5]; # Baselevel currently running
my $baselevel = $ARGV[6]; # Baselevel currently running
my $patches = $ARGV[7]; # List of installed patches
my $insploredir = $ARGV[8]; # Directory name containing the decompressed Insplore
# Define local variables, global in this program though
my %local_hash = (); # Hash to store local stuff
my $lptr = \%local_hash;
my $save_debug = $common->{debug}->{level};
# In order to facilitate debugging and see the structure of the hash, uncomment the following 2 lines.
# $common->{debug}->{level} = TRACE_MEMORY;
# $common->dump_memory($ptr, "cfganal_vv: ptr");
# Report issues using the following method:
# $common->report_cfganal_issue($syssn, $type, $vvid, <column>, "Comments go here", <analysis_code>, $cageid, <analysis_code_p1>, <analysis_code_p2>, ..);
$common->trace(TRACE_ROUTINES, "---> cfganal_vv $type, $syssn, $model, $version, $baselevel, $patches");
foreach my $vvid (sort keys(%{$ptr})) {
# Your tests per vv go here.
}
$common->trace(TRACE_ROUTINES, "<--- cfganal_vv");
$common->{debug}->{level} = $save_debug;
return 1;

## Slide 21: iNex processing, an in-depth explanation
Phase4: Break-Out routines
Break-Out routine is a text file, executed during the analysis phase.
Standardized calling interface. Standardized feedback interface back into iNex.
Findings are posted in related worksheet, offending object is highlighted and posted with a comment.
Findings are posted in “Overview” worksheet in Analysis section.
Notes: The shown screenshots are provided as examples.

## Slide 22: iNex processing, an in-depth explanation
Phase4: Break-Out routines
Implemented configuration checks (V1.22-1):
Node: F- and T-class Data Cache DIMM, IPL5 on V-class, Cache Availability 100%
PD: Seagate Eagle, Hitachi MarsK based upon serial numbers, disk drive firmware and InFormOS release. Hitachi CobraE based upon disk drive firmware
CPG: Growth values meeting minimum requirements, deviations from default values
Captures: Number of occasions of ct_mgmt_get_port_info, sdt_cdb_retry_func, els_ct_timeout, scsi_send_cmnd_async, scsi_send_cmnd_retry, sdt_getlbastatus, excessive RTPG events due to down-rev Host Explorer.
Events: Failure scenario’s of Hitachi MarsK and CobraE drives
RCopy: Path Management policy for sync RCGroups with members presented to ESX servers.
Ports: iSCSI ports configured with fixed IP addresses, Persistent Port.

## Slide 23: iNex Spreadsheets

## Slide 24: iNex spreadsheets
Introduction
A “spreadsheet” is a file containing multiple worksheets.
Output is grouped in 3 spreadsheets:
      “events”, which contains the output of events as well as captured data.
      “lesb”, which contains the LESB / PEL information per port.
      “main”, which contains all configuration information, and other, relatively small, worksheets.
      All spreadsheets contain Visual Basic macros, thus enabling single keystrokes for frequently used operations.
      All spreadsheets contain (relative) hyperlinks, allowing the spreadsheets to be moved to a different location after creation.
      A dedicated spreadsheet is created related to Node panic information.
  Compressed output (“Grouping” in MS-Excel) is used to provide a better
        overview across all object of the same type, and allows to zoom in into a specific object.
Indication that grouping is used.
Click on “1”  no details are shown
Click on “2” all details are shown for al objects
Click on “+”  all details are shown for single object

## Slide 25: iNex Spreadsheets
List of available worksheets (*.main.xlsm spreadsheet)
“Overview”. Primary worksheet. Contains system overview, check health output, analysis overview, hyperlinks to other worksheets. All other worksheets contain hyperlink back to this worksheet.
“Index”. Provides hyperlinks grouped around object type. The hyperlinks point to specific information category.
“Cluster”. Provides information on cluster level. Based upon various “showsys”, “showversion”, “showlicense”, “showsysmgr”, “shownet”, “showtocgen”, “showtoc”, “showuser”, “showuseracl”, “showuserconn”, “showauthparam”, “controlencryption –status”, “showpatch –history” commands.
“Nodes”. Provides information on nodes, hence based upon various “shownode”, “showeeprom”, “showbattery”, “shownodeenv”, “shownet”, “showdate” commands . Contains hyperlinks to Nemoe event logs, Nemoe Power Logs, BIOS Banners, BIOS Message Logs, Linux process info (ps –ef), Linux memory info (meminfo) on a per-node base. Automatic flagging of abnormal status / state fields and LED patterns.
“Port x– y”. Provides information on ports in the range x:0:0 – y:15:15. Based upon various “showport” , “showrctransport” commands. Contains hyperlinks to LESB / PEL information if available on a per port base. Automatic flagging of abnormal status / state / speed fields. Information is compressed, color coded. Per default, free ports are not displayed.
“SAN Ports”. Provides information on SAN from 3PAR point of view. Based upon various “showportdev n:s:p” commands. Automatic flagging of differences in output of “showportdev” commands

## Slide 26: iNex Spreadsheets
List of available worksheets (*.main.xlsm spreadsheet)
“Cage Data”. Provides information on cages. Based upon various “showcage” commands, except “showcage –e”. Layout is optimized per cage type. Automatic flagging of abnormal status / state fields and LED patterns.
“Cage Comms”. Provides information on back-end communication to cages and disk drives. Based upon “showcage –e” output for non-EOS systems, “showportperl –both n:s:p” command for EOS systems. Layout is optimized per cage type.
“PhysicalDisks”. Provides information per disk drive. Based upon various “showpd” and “toctool –l” commands. Automatic flagging of abnormal status / failed chunklets / firmware. Contains ‘databars’ to show remaining life left and capacity used.
“CPGs”. Provides information per CPG. Based upon various “showcpg” commands. Contains ‘databars’ to show used vs allocated raw capacity. Contains pie-chart to compare user data within CPGs
“LogicalDisks”. Provides information per LD, including PDs used by a LD. Based upon various “showld”, “showpdch” and “showldch” commands. Automatic flagging of abnormal status.
“VirtualVolumes”. Provides information per VV, SCSI reservations and QoS. Based upon various “showvv”, “showvvset”, “showvlun”, “showvvcpg”, “showvvmap”, “showqos”, “showrsv”, “showrcopy -d” commands. Automatic flagging of abnormal status. Contains ‘databars” to show ratio between allocated vs reserved user space, as well as, per VV, the ratio of allocated space versus allocated space per CPG. Information per default displayed in compressed format.

## Slide 27: iNex Spreadsheets
List of available worksheets (*.main.xlsm spreadsheet)
“Hosts and LUNs”. Provides information on Hosts and their presented LUNs, as well as host persona definitions (release dependant). Information per default displayed in compressed format. Based upon various “showhost”, “showhostset”, “showvlun” command. Contains matrix per HBA, which indicates on which host ports the VLUNs are presented.
“RemoteCopy”. Provides information on Remote Copy, and non-RC targets. Based upon “showrcopy –d”. “showtarget” commands. Automatic flagging of abnormal status / state / unknown targets Information per default displayed in compressed format.
“Memory”. Provides time-stamped information on memory usage per node. Based upon “Memory usage information” events, which are part of “showeventlog –d –debug –oneline” command. Automatic flagging when (release and model dependent) thresholds are exceeded.
“Tasks”. Provides information on tasks. Based upon “showtask” command as well as /pr_mnt/tasks_data/tasks_detail_* files. Provides ability of “OpenFile” macro to show tasks_detail_*.txt file, which is created during iNex processing (Phase2).
“SR AO Config and Events”. Provides information on AO and SR configuration, scheduled tasks, and history of events related to AO. Based upon “showaocfg”, “showsr”, “showsched –all” commands as well as “/pr_mnt/scheduler_table” file and “CLI command executed” events, which contain “createaocfg”, “compactcpg”, “startao”, “srrgiodensity” or “createsched”.

## Slide 28: iNex Spreadsheets
List of available worksheets (*.main.xlsm spreadsheet)
“SR AO Logs”. Provides a time-stamped (reversed order) sequence of log entries, as found in the /var/log/tpd/srsampler, /var/log/tpd/srdatac, /var/log/tpd/srdatastop, /var/log/tpd/ldrgsampler files on each node.
“SR AO Data Statistics”. Provides several graphs and tables, which provide insight into AO data movement, data locality. Based upon the “showaomoves –btsecs -1d”, “srrgiodensity –btsecs” commands or any file containing “aomoves” or “iodensity” in the filename.
“PD Capacity Charts”. Provides several graphs showing the usage level of PDs, sorted per device type, as well as usage of device type per node. Based upon various “showpd” commands.
“PD AscAscq”. Provides an overview, per PD, of the Asc/Ascq’s logged per disk drive. Based upon the “Disk Event” entries in the “showeventlog –d –debug –oneline” command. Optional worksheet, only present in case these events are detected. Information per default displayed in compressed format
“PD Chunklets”. Provides 2 overviews related to PD chunklets. Based upon “showspare”, “showpdch –a” commands as well as the “Disk Event” entries in the “showeventlog –d –debug –oneline” command. Optional worksheet, only present in case these events are detected or in case used spare chunklets or relocated chunklets exist.
“Port_N_S_P_SAS_Domain”. Provides an overview of the SAS Domain devices and cabling. Based upon the “showportdev –sas n:s:p” command.
“iSCSI stats”. Shows the iSCSI statistics and error counts. Based upon the “statiscsi –fullcounts –iter 1” command. Optional worksheet, only present in case InServ is configured for iSCSI.
“UpDown”. Shows the Inserv cluster transitions by nodes appearing and disappearing from the cluster.

## Slide 29: iNex Spreadsheets
List of available worksheets (*.events.xlsm spreadsheet)
“Events Summary”. Provides an overview of number of “event skeletons” logged per object. Sorted per object per event severity. Information per default displayed in compressed format.
“EventLog”. Provides a time-stamped (reverse order) overview of the logged events and alerts. Based upon the “showeventlog –d –debug –oneline”, “showeventlog –d –fprefix events nd”, “showeventlog –d –fprefix events al” commands. Contains hyperlinks back into configuration data in case an object is mentioned in an event.
“Alerts”. Provides an overview of the outstanding alerts. Based upon the “showalert -d” command.
“Captured Log Data – Summary”. Provides an overview of the capture definition strings, which resulted in a hit, the number of times the string was found as well as the (short) filename and node-name. Based upon the <INEX_HOME>\defs\capture_definitions.txt file.
“Captured Log Data”. Provides a time-stamped overview of the processing of the <INEX_HOME>\defs\capture_definitions.txt file. Allows the “OpenFile” macro to open the file, in which the string is encountered and jump directly to the line number where the string is located.
“Hosts Events Summary”. Provides an overview of the event categories logged per host. Shows per host are counts of path related events, SCSI AscAscq events and SCSI Reservation events. Information per default displayed in compressed format. Based upon “showeventlog –d –debug –oneline” command and specific event categories.
“Hosts Events List”. Provides a time-stamped overview of events logged per host. Information per default displayed in compressed format. Based upon “showeventlog –d –debug –oneline” command and specific event categories.

## Slide 30: iNex Spreadsheets
List of available worksheets (*.lesb.xlsm spreadsheet)
“Port_N_S_P_SAS_PEL” . Provides a time-stamped (reversed order) overview of the SAS port and SAS device error counters. Information per default displayed in compressed format. Based upon the “pr_mnt/portpel_history_*” files. Worksheet is available on InServs with a SAS back-end only.
“Port_N_S_P_LESB”. Provides a time-stamped (reversed order) overview of the error counters on FC-based host, rcfc, peer, and disk ports. The information shows the deltas of the error counters compared to the previous sample. Lists observed devices throughout the timespan, which is 4 x the “monitor window”, so per default 4 x 7 = 28 days. Information per default displayed in compressed format. Based upon “showportlesb –hist n:s:p” commands

## Slide 31: iNex Spreadsheets
Available Macros
iNex generates Microsoft Excel spreadsheets with included Visual Basic macros .
Macro files are:
    Textual representation have the *.txt extension, located in <INEX_HOME>\defs\macros
    Binary representation is the “<INEX_HOME>\defs\iNex_macros.bin” file. If binary representation is present, it is auto-loaded in all spreadsheets.
Available macros:
    “Auto_Open”. Used by MS Excel to start macro execution upon opening of spreadsheet. Do *NOT* change.
    “AutoRun”. Anchor macro of iNex. Calls other macros and contains hot-key definitions.
    “CreateDataBars”. Creates the databars on specific worksheets. Do *NOT* change.
    “OpenFile”. Opens a file based upon information found in row. Change during configuration phase to match text editor. Referenced using hot key Ctrl+Shft+G.
    “DeleteThisAndSimilarRowsLikeCurrentCell”. Macro which removes rows from the current worksheet, which have the same content as the current cell. Referenced using hot-key Ctrl+Shft+D.
    “HideThisAndSimilarRowsLikeCurrentCell”. Macro which hides rows on the current worksheet, which have the same content as the current cell. Referenced using hot-key Ctrl+Shft+H.
    “UnHideAllRows”. Undo of “HideThisAndSimilarRowsLikeCurrentCell”. Referenced using hot-key Ctrl+Shift+U.
    “Find_Yellow_Interior”. Locates the next cell which is yellow marked, even if cell is outside screen or in compressed area. Referenced using hot-key Ctrl+Shft+M
Notes: iNex V1.22 automatically creates the <INEX_HOME>\defs\iNex_macros.bin file if it does not exist. Subsequent invocations of the iNex program will therefor use the binary representation of the macros and not start-up Ecel for every generated spreadsheet.
Hence if new macros are added, the <INEX_HOME>\defs\iNex_macros.bin file must be deleted prior to running iNex again.
File can be re-generated / picked up by using the Tools menu in the GUI (V1.22 onwards).
In the OpenFile macro (in <INEX_HOME>/defs/macros), locate the following lines:
' ------------------------------------------------------------------------------
'
' The command line generated to start the editor is:
' 'cEditor <file><cLineNrOption><linenr>'
' It may be required to add a space to the cLineNrOption variable
'
' Uncomment the 2 lines related to your editor of choice.
'
' PSPad on 32-bit
' cEditor = "C:\Program Files\PSPad editor\PSPad.exe "
' cLineNrOption = " -"
'
' PSPad on 64-bit Windows
cEditor = "C:\Program Files (x86)\PSPad editor\PSPad.exe "
cLineNrOption = " -"
'
' For Vim/gVim on 32-bit Windows
' cEditor = "C:\Program Files\Vim\vim72\vim.exe "
' cLineNrOption = " +"
'
' For Vim/gVim on 64-bit Windows
' cEditor = "C:\Program Files (x86)\Vim\vim72\vim.exe "
' cLineNrOption = " +"
'
' ------------------------------------------------------------------------------
NOTE: When using Windows8, <INE_HOME>\defs\iNex_macros.bin MUST be used.

## Slide 32: iNex Spreadsheets
Overview worksheet
checkhealth color coded output (compressed) and
‘showsysmgr’ output
Links to other worksheets
Insplore date & time, system name, InServ Type, Inserv serial number
Version information
Nr of objects and distribution across nodes
Analysis Summary
Notes: iNex uses the following rules to determine the severity of checkhealth messages:
Checkhealth does not complain for this component  Status OK, color Green
Checkhealth complains for this component:
  Contains the words “failed”  Status Critical, color Red
  Contains the words “down”, “error”, “flusher speed”  Status Error, color Orange
  In all other cases  Status Warning, color Yellow
Worksheet names which are “yellow marked”, contain objects which report an abnormal status.

## Slide 33: iNex Spreadsheets
Overview worksheet
Analysis Summary
After following hyperlink
“Analysis Summary”
Notes: The codes listed are the “analysis codes”, which are defined in the <INEX_HOME>\defs\analysis_definitions.txt file.
The severity corresponds to the severity defined for this analysis code.
The %p1%, %p2% etc are filled in during runtime.
Analysis codes which are linked to a CFI (so with CFI%<number>%) allow for an automatic upload of the GR8 / SI case number to the central CFI database.
The output in the analysis section is always compressed. One will need to click the “+” in front of the row in order to see the actual message.

## Slide 34: iNex Spreadsheets
Capture related worksheets
2 worksheets:
  Capture Log Data. Contains a time-stamped overview of all occurrences, within the monitor window, of the strings specified in <INEX_HOME>\defs\capture_definitions.txt in the specified files. The overview is in chronological order.
        Worksheet allows the “OpenFile” macro to open file and jump to line-number where the string is encountered.
    Captured Log Data – Summary. Contains an overview of the number of occurrences, within the monitor window, of the strings specified in <INEX_HOME>\defs\capture_definitions.txt in the specified files.
Capture definitions may occur, via mapping on analysis code, in the “Analysis Overview” on the “Overview” worksheet.

## Slide 35: iNex Spreadsheets
Capture related worksheets
Analysis Overview
Capture Log Data - Summary
Capture Log Data

## Slide 36: iNex Spreadsheets
Capture related worksheets
Select Cell on row
Invoke “OpenFile” macro (Ctrl+Shft+G)
Pop-up box will appear

## Slide 37: iNex Spreadsheets
PD related worksheets
4 worksheets:
Physical Disks, provides all configuration information related to a disk drive. Contains ‘databars’ for “life left” of a disk drive as well as occupancy level.
PD Capacity Charts, provides several graphs related to balancing of PDs and PD types across node-pairs, as well as balancing of data across PDs of the same type.
PD AscAscq, provides an overview, sorted on PD position (Cage:Mag:Disk), with number of AscAScq’s logged by the PD as well as actual AscAscq’s.
PD Chunklets, provides 2 unrelated overviews:
    PDs with relocated chunklets, which is an overview of all temporary relocated chunklets, where they are now as well as their original location.
    PDs with chunklets reporting IO errors, which is an overview of PD chunklets using PD blocks, which report AscAscq. The overview contains the mapping of PD Ch  LD Ch whenever possible.

## Slide 38: iNex spreadsheets
PD related worksheets. “Physical Disks”
databars
This worksheet shows:
PD Position,
PD back-end info,
PD device info (vendor, model, type, speed, firmware, serial number, WWN, state, detailed state, temp, life-left),
Capacity Info (raw, used, free, percent),
Error Counts (read, write, correctable y/n),
Chunklet information (normal, spare, used, unused, OK, Fail, UnInit, UnAvailable)
TOC information (not shown above, “toctool –l” output)

## Slide 39: iNex spreadsheets
PD related worksheets. “PD Capacity Charts”
Overview of number of PDs,
Total / Used / Free capacity
balancing across all nodes
Overview of number of types of PD,
Total / Used / Free capacity
Balancing across all nodes and PDs

## Slide 40: iNex spreadsheets
PD related worksheets “PD AscAscq”

## Slide 41: iNex spreadsheets
PD related worksheets “PD Chunklets” 1/2
Lefthand part of worksheet
Overview of relocated chunklets and where
they originate from. Sorted on PD position,
contains PD Ch  LD Name and LD Ch

## Slide 42: iNex spreadsheets
PD related worksheets “PD Chunklets 2/2”
Right-hand part of worksheet
Overview of IO errors logged for PD blocks, which
are mapped onto PD Ch  LD Name and LD Ch.
Includes IO error count per PD block and
PD Ch.
NOTE: The graph shows that the CmdStatus Column (“AN”) filters out TE_HWERR, only showing TE_CRC, TE_FAIL, TE_MEDFAIL

## Slide 43: iNex Spreadsheets
Host related worksheets
4 worksheets:
SAN Ports. Provides an overview of the SAN connected devices from a host, rcfc, peer port point of view. Contains count of nr of Initiators per host port. Based upon the “showportdev –all” and showportdev –ns” commands.
Hosts and LUNs. Provides an overview presented LUNs, HBAs, hostsets, iSCSI host definitions per host.
Hosts Events Summary. Provides an overview of number of event types logged per server per host port. Optimized to be used in cases where servers lost access to the InServ.
Hosts Events List. Provides a chronological overview of events, related to a server. The output is sorted per server. Optimized to be used in cases where servers lost access to the InServ.

## Slide 44: iNex Spreadsheets
Host related worksheets (“SAN Ports”)
This worksheet lists:
SID of the HBA, Index of the SID (in case same SID is observed on different host ports, but not same HBA
Indication if SID is listed in showportdev –all and showportdev –ns as well as different between both.
Port WWN and Node WWN
Type (port, host, rcfc), Server name / InServ host port, persona, list of host ports HBA is logged into
Number of initiators per host port.

## Slide 45: iNex Spreadsheets
Host related worksheets (“Hosts and LUNs”)
Nr of VVs presented to server
Nr of HBAs in server
Nr of host ports where HBA logged into.

## Slide 46: iNex Spreadsheets
Host related worksheets (“Hosts and LUNs”)
Detailed output shows:
- LUN nr and associated VV
- Server HBA WWNs
- Matrix of Nodes and Ports
“Y” means: VLUN presented
“-” means: VLUN not
presented
“x” means: no host port

## Slide 47: iNex Spreadsheets
Host related worksheets (“Hosts Events Summary”)
Path Lost/Normal event count
Asc/Ascq/Skey
event count
SCSI reserve / release
event count
Notes: 3 independent overviews:
Path Lost / Normal event count
AscAScQ/Sensekey event count
SCSI reserve/release event count
Default output compressed
Use “+” to see the details.
iNex will indicate which Asc/Ascq values can be ignored (grayed) and which ones not (black). Same applies to SenseKey and SCSI Status values.
The first row (rows 5, 31, 46, 59, 72, 85, 98, 111, 124, 137, 150 in the example above) provides the overall numbers per server; the detailed
Output lists the actual number encountered per port and per Asc/Ascq/SKey

## Slide 48: iNex Spreadsheets
Host related worksheets (“Hosts Events List”)
Initial display is compressed and shows total event count / host.
Detailed display shows chronological ordered listing of events for that server

## Slide 49: iNex Spreadsheets
SR AO related worksheets
3 worksheets:
SR AO Config and Events. Provides an overview of the actual AO configuration, SR configuration, list of the scheduled tasks and events related to AO objects.
SR AO Logs. Provides a chronological overview of the log entries of the SR and AO related processes on all nodes.
SR AO Data Statistics. Provides graphical representations on statistics of AO data movement. These statistics are used by AO to determine the next set of region moves.

## Slide 50: iNex Spreadsheets
SR AO related worksheets (“SR AO Config and Events” 1/2)
SR AO Config and Events
AO configurations
SR node and
DB table sizes

## Slide 51: iNex Spreadsheets
SR AO related worksheets (“SR AO Config and Events” 2/2)
Overview of all schedules tasks
Overview of SR AO related events

## Slide 52: iNex Spreadsheets
SR AO related worksheets (“SR AO Logs”)
Notes: This is the merged output, reversed time order, of the /var/log/tpd/srsampler, /var/log/tpd/srdatac, /var/log/tpd/srdatastop, /var/log/tpd/ldrgsampler files on each node.

## Slide 53: iNex Spreadsheets
SR AO related worksheets (“SR AO Data Statistics 1/5”)
Combined overview of all AO region moves between the tiers.
Notes: This can be a very busy worksheet, containing lot of graphs.
Most graphs are per AO configuration; however “Adaptive Optimization Configurations” and “IO versus Space distribution” are graphs, which have all AO configurations in one combined view.
The graph on this slide is based upon the output of “sraomoves –btsecs -1d”
Start Time: 2014-01-23 11:02:17 PST (1390503737)
End Time: 2014-01-24 11:02:17 PST (1390590137)
Id Name SrcTier DstTier Space MovedMB
2 AO_Databases 0 1 adm 47776
2 AO_Databases 0 1 usr 7103232
2 AO_Databases 0 2 adm 28608
2 AO_Databases 0 2 usr 2594304
2 AO_Databases 1 0 adm 47584
2 AO_Databases 1 0 usr 4414848
2 AO_Databases 1 2 adm 8544
2 AO_Databases 1 2 usr 8839040
2 AO_Databases 2 0 adm 19136
2 AO_Databases 2 0 usr 2570752
2 AO_Databases 2 1 adm 15040
2 AO_Databases 2 1 usr 2558336
3 AO_VMs 0 1 adm 129600
3 AO_VMs 0 1 usr 2829440
3 AO_VMs 0 2 adm 4704
3 AO_VMs 0 2 usr 60928
3 AO_VMs 1 0 adm 141440
3 AO_VMs 1 0 usr 6961536
3 AO_VMs 1 2 adm 10016
3 AO_VMs 1 2 usr 1315200
3 AO_VMs 2 0 adm 7840
3 AO_VMs 2 0 usr 584960
3 AO_VMs 2 1 adm 58880
3 AO_VMs 2 1 usr 15670784
....

## Slide 54: iNex Spreadsheets
SR AO related worksheets (“SR AO Data Statistics 2/5”)
Overview, per AO configuration of the data movement To / From a tier versus the size of the CPG on that tier.
Notes: This output is based upon the “sraomoves –btsecs -1d” output as well as several showcpg commands.

## Slide 55: iNex Spreadsheets
SR AO related worksheets (“SR AO Data Statistics 3/5”)
IO region density report per AO configuration,
Non-cumulative view. Based upon “srrgiodensity –btsecs -1d <AO cfgname>”

## Slide 56: iNex Spreadsheets
SR AO related worksheets (“SR AO Data Statistics 4/5”)
IO region density report per AO configuration,
cumulative view. Based upon “srrgiodensity –btsecs -1d <AO cfgname>”
Calculation table for # of required SSDs to sustain I/O load for this AO configuration

## Slide 57: iNex Spreadsheets
SR AO related worksheets (“SR AO Data Statistics 5/5”)
Combined overview of the effectiveness of AO
For all AO configurations.
Known as the “IO versus Space distribution” graph.

## Slide 58: iNex Spreadsheets
VV related worksheets
2 worksheets:
“Virtual Volumes”, which provides an overview of the VV characteristics, including presentation to Hosts and CPG distribution, SCSI reservations, QoS definitions, associated snapshots, physical copies
“Remote Copy”, which provides an overview of the RC configuration, including RCGroups, Links, unknown targets, and overall RC status.

## Slide 59: iNex Spreadsheets
VV related worksheets (Virtual Volumes (1/5)
VV Name, VVID, Domain, Vvset and VV Tree (in names)
VV Type, presented vs allocated capacity, WW LUN ID, State,
Usr CPG, Snap CPG, RCGroup, hyperlinks to SCSI reservations and QoS definitions.
VV presentation,
Active / Standby paths
Notes: Childs start with a “_”. The number of “_” chars defines how deep in the VV Tree the child is located.

## Slide 60: iNex Spreadsheets
VV related worksheets (Virtual Volumes (2/5)
VV Tree (using IDs,
Sometimes names
VV size info (“showvv –r” output)
Notes: Slide 5 of the Virtual Volumes will show a VV tree using snapshots and pcopies.

## Slide 61: iNex Spreadsheets
VV related worksheets (Virtual Volumes (3/5)
VV creation date,
VV CPG usage
Notes: iNex uses the “showvvmap” (InSplore) or “showvvcpg” (config.*.0001) to be able to determine how much data is allocated per CPG.
Very useful information in case of configurations using AO.

## Slide 62: iNex Spreadsheets
VV related worksheets (Virtual Volumes (4/5)

## Slide 63: iNex Spreadsheets
VV related spreadsheets (“Virtual Volumes” 5/5)
Example of VV Tree
Notes: Corresponding showvv output:
----- showvv -----
---------Rsvd(MB)--------- --(MB)---
Id Name Domain Prov Type CopyOf BsId Rd -Detailed_State- Adm Snp Usr VSize
1 .srdata - full base --- 1 RW normal 0 0 81920 81920
0 admin - full base --- 0 RW normal 0 0 10240 10240
3 Avdhesh_test1 - full base --- 3 RW normal 0 0 10240 10240
24572 eua1a3_vg1a0 - tpvv base --- 24572 RW normal 512 16768 97280 102400
19280 vvcp.24572.24575 - snp vcopy eua1a3_vg1a0 24572 RO normal -- -- -- 102400
24575 eua1a3_vg1a0.pc - tpvv pcopy vvcp.24572.24575 24575 RW normal 512 16256 101376 102400
19286 eua1a3_vg1a0.snap - snp vcopy eua1a3_vg1a0.pc 24575 RW normal -- -- -- 102400
29236 eua1a3_vg1a0.1 - tpvv base --- 29236 RW normal 512 1024 2048 102400
19281 vvcp.29236.19855 - snp vcopy eua1a3_vg1a0.1 29236 RO normal -- -- -- 102400
19855 eua1a3_vg1a0.1.pc - tpvv pcopy vvcp.29236.19855 19855 RW normal 512 1024 2048 102400
19287 eua1a3_vg1a0.1.snap - snp vcopy eua1a3_vg1a0.1.pc 19855 RW normal -- -- -- 102400
19851 eua1a3_vg1a0.2 - tpvv base --- 19851 RW normal 512 1024 1024 1024
19282 vvcp.19851.19884 - snp vcopy eua1a3_vg1a0.2 19851 RO normal -- -- -- 1024
19884 eua1a3_vg1a0.2.pc - tpvv pcopy vvcp.19851.19884 19884 RW normal 512 1024 1024 1024
19288 eua1a3_vg1a0.2.snap - snp vcopy eua1a3_vg1a0.2.pc 19884 RW normal -- -- -- 1024
24573 eua1a3_vg1a0a - tpvv base --- 24573 RW normal 512 1024 21504 102400

## Slide 64: iNex Spreadsheets
VV related worksheets (“Remote Copy” 1/3)
1:1 sync
SLDR
RCGroup Policies
RCGroup local / remote members,
RC sync status / members, associated snapshots
RCGroup ID, Name, Role, Mode, State and Target
Notes: This worksheet is based upon the output of the “showrcopy –d” command.

## Slide 65: iNex Spreadsheets
VV related worksheets (“Remote Copy” 2/3)
RC overall status, status of RCFC / RCIP ports, status of RC links

## Slide 66: iNex Spreadsheets
VV related worksheets (“Remote Copy” 3/3)
RC overall status, status of RCFC / RCIP ports, status of RC links SLDR configuration

## Slide 67: iNex Spreadsheets
FC and SAS related worksheets
6 worksheets:
“Ports x – y”. Provides and overview of the FC, SAS, RCIP and iSCSI ports and their characteristics on Node “x” to Node “y”.
“Cage Data”. Provides an overview of the cages in the system, their configuration, and connectivity to the nodes. Layout and information dependent on cage type.
“Cage Comms”. Provides an overview of the error counters between the nodes, the cage and the individual disk drives. Layout and information dependent on cage type.
“Port n:s:p LESB”. Provides a chronological overview of the differences in LESB counters per port per observed device. Not for SAS-based initiator ports.
“Port n:s;p SAS PEL”. Provides a chronological overview of the SAS error counters between the nodes, the cages and the individual disk drives. Only for SAS-based initiator ports.
“Port n:s:p SAS Domain”. Provides an overview of the SAS domain for a SAS port. Also contain the actual wiring diagram, including checks for proper wiring. Only for SAS-based initiator ports.

## Slide 68: iNex Spreadsheets
FC and SAS related worksheets (“Port x - y”)
Hyperlink to LESB or SAS PEL
Worksheet of this port
Notes: More information on SPF’s is available at higher row numbers.
NOTE: Color coded per port type:
blue  Host / iSCSI port
black  Disk port
green  RCFC / RCIP port
purple  Peer port
magenta  FCoE port
gray  Free port
NOTE: “Free” ports are per default not displayed.
NOTE: Ports which are set to a fixed speed are highlighted as well, as “auto” is preferred.
Port Names are hyperlinks to LESB or SAS PEL counters

## Slide 69: iNex Spreadsheets
FC and SAS related worksheets (“Cage Data” (DC4 cage – T- and V-Class))
Notes: Pictures should be placed subsequent to each other.
As for the drive magazines: it only displays the filled magazine slots, not the empty ones. Mag5 for example is not used in this system.

## Slide 70: iNex Spreadsheets
FC and SAS related worksheets (“Cage Data” (DCN1 / DCS1 EOS))
Cage position in SAS domain on Port 1:01
Cage position in SAS domain on Port 0:01
Notes: Cabling can be derived from here or , as later on shown, from the “Port n:s:p SAS Domain” worksheet.
Of the SAS address, only the last 8 characters are shown. The full address is there, just click on the cell.

## Slide 71: iNex Spreadsheets
FC and SAS related worksheets (“Cage Comms” (DC4 cage – T- and V-Class))
Notes: Use this worksheet in case of back-end communication issues.
The “-” mean that the counter is zero, resulting in the non-zero counters to stand out.
Just scroll through the worksheet to see if there are any disks with non-zero counters.
If not, could be an IFC, SFP in Node or IFC or cable.

## Slide 72: iNex Spreadsheets
FC and SAS related worksheets (“Cage Comms” (DCN1 / DCS1 EOS))
Notes: Use this worksheet in case of back-end communication issues.
The “-” mean that the counter is zero, resulting in the non-zero counters to stand out.
Just scroll through the worksheet to see if there are any disks with non-zero counters.
My experience is that TE_DIF errors will not show up here. The “Port n:s:p SAS PEL” worksheet is in those case far more helpful.

## Slide 73: iNex Spreadsheets
FC and SAS related worksheets (“Port n:s:p LESB 1/2”)
Lists N:S:P, Port WWN, Port Type, Port SID, Hyperlink back to port on “Ports x – y” worksheet
Sum of delta in LESB counters on specific date/time
Notes: The bottom row shows the initial counters.
If you click on the “+” signs, one will see the delta in LESB counters per discovered device. See next slide.
The time window is 4 x the monitor window, so typically 4 x 7 = 28 days.

## Slide 74: iNex Spreadsheets
FC and SAS related worksheets (“Port n:s:p LESB 2/2”)
Lists the encountered devices / hosts on this port
Lists the encountered devices / hosts on this port, their presence / absence / appearance in this time sample and the delta in LESB counters compared to previous time sample.
Lists the encountered devices / hosts on this port, their initial WWN, SID and LESB counter
Notes: Devices / Hosts / Remote Systems are tracked during processing.
The meaning of the columns C – L is:
Blank  No value
“-”  No change compared to difference time sample
“x”  Device / Host / RCFC not present in this time sample
Number  Delta of counter compared to previous time sample
WWN  Device / Host / RCFC newly appeared in this time sample using WWN
Alpa  Device newly appeared in this sample using Alpa (for “disk” port types only)
xx-yy-zz  Host / RCFC newly appeared in this same on SID xx-yy-zz (for non-disk port
types only)

## Slide 75: iNex Spreadsheets
FC and SAS related worksheets (“Port n:s:p SAS PEL 1/2”)
Notes: Lists the total number of errors per time sample

## Slide 76: iNex Spreadsheets
FC and SAS related worksheets (“Port n:s:p SAS PEL 2/2”)
Notes: When clicking on the “+” sign, you will see the SAS error counters per SAS device per time sample.

## Slide 77: iNex Spreadsheets
FC and SAS related worksheets (“Port n:s:p SAS Domain”)
Actual SAS cable wiring diagram

## Slide 78: iNex Spreadsheets
Miscellaneous worksheets
6 worksheets:
“Cluster”. Provides an overview of system wide information, like system parameters, licensing, LDAP configuration, User connections, IOCTL information, sysmgr status, detailed version information.
“Nodes”. Provides an overview of all nodes in the system including their characteristics
“LogicalDisks”. Provides an overview of all LDs including their characteristics and PD mapping (if available).
“Memory”. Provides a chronological overview of the memory usage per node during the monitor window.
“Tasks”. Provides a chronological (reversed order) overview of the start- and completion time of a task, completion status and links to the task details.
“iSCSI stats”. Provides an overview of the iSCSI statistics, including error counters.
“UpDown”. Provides chronological overview of node membership of Inserv cluster.

## Slide 79: iNex Spreadsheets
Miscellaneous worksheets (“Cluster”)
Notes: Very busy slide showing system-wide and user information.
Typically used to pick up the master node, update history and, in user connections, the IP address of the SP, as the active user connection is marked with a “*”

## Slide 80: iNex Spreadsheets
Miscellaneous worksheets (“Nodes”)
Hyperlinks to Nemoe files, BIOS files and Linux process / memory information
If environmental issues are detected, they will be reported here
Notes: Highlighted dates mean that they occurred within the monitor window, so within the 7 days window.
In this example, a firmware upgrade was attempted less than 7 days ao.
Note that the upgrade failed, as Node0 runs 3.1.3, while the other ones run 3.1.2.
This slide will contain info on :
Actual node hardware itself
MCU
File system usage
Memory
Power
Batteries
Fan
Network ports
Internal HDD
Etc, basically everything listed in the shownode –verbose output.

## Slide 81: iNex Spreadsheets
Miscellaneous worksheets (LogicalDisks 1/2)

## Slide 82: iNex Spreadsheets
Miscellaneous worksheets (LogicalDisks 2/2)
Mapping of LD  PDs
(not always part of InSplore)

## Slide 83: iNex Spreadsheets
Miscellaneous worksheets (“Memory”)
High Level Info
Detailed Info

## Slide 84: iNex Spreadsheets
Miscellaneous worksheets (“Tasks” 1/2)

## Slide 85: iNex Spreadsheets
Miscellaneous worksheets (“Tasks” 2/2)
Using the “OpenFile” macro
(Ctrl+Shft+G)

## Slide 86: iNex Spreadsheets
Miscellaneous worksheets (“iSCSI stats”)
Notes: This worksheet only exists is the configuration contain iSCSI ports.
Mainly check the error counters, not so much the statistics, unless there is a significant different / port.

## Slide 87: iNex Spreadsheets
Miscellaneous worksheets (“UpDown”)
Crash Dump generation
TPD Version loaded
Node Up/Down
according /var/log/messages
Node Up/Down
according /var/log/tpd/sysmgr

## Slide 88: iNex Spreadsheets
Index

## Slide 89: auto_update how it really (not) works

## Slide 90: auto_update: how it really (not) works
Introduction
iNex is distributed on HP Intranet only
    Account of ftp.usa.hp.com still exists, but will expire end of CY2014.
      Last version posted only contains auto_update, which, after installation, points user to HP Intranet distribution points.
    Distribution server is fs1.bel.hp.com, which is ‘rsync-ed’ to regional distribution servers.
Check for update algorithm:
    Only runs once / day, determined by creation date+time of <INEX_HOME>\log\auto_update.log, immediately after startup of the GUI or CLI.
    Determines if connected to HP IntraNet
      NO: Will access ftp://tool4you:3Partool@ftp.usa.hp.com (and typically find no update)
      YES: Will access regional distribution server based upon login domain of user.
        If update is found: it will download it and alert user of new version.
        If no update is found: Is this a Monday: If not, done, and re-try tomorrow. If yes, access ftp://3PARtools:3PaRr*cksing@fs1.bel.hp.com/storage/3PAR/inex
Notes: If you need to retry auto_update, just remove the <INEX_HOME>\log\auto_update.log file and restart the GUI.
The Linux version uses just FTP access to either ftp.usa.hp.com or fs1.bel.hp.com
The check for connection to the HP IntraNet is as follows;
Check if the server uses an IPv4 address on the 15.*.*.* or 16.*.*.* network. If there is an IPv4 address within
  Then the server is assumed to be connected to the HP IntraNet.
In case there is no IPv4 address with a 15.* and 16.* address, the DNS name of the server is checked.
  If the DNS name ends on “hpqcorp.net”, then it is assumed that the server has a trust relationship
  With the HP domain and that Direct Access is available and configured.

## Slide 91: auto_update: how it really (not) works
Distribution servers
FTP access (Linux and Windows):
    ftp://3PARtools:3PaRr*cksing@fs1.bel.hp.com/storage/3PAR/inex or
    ftp://fs1.bel.hp.com/3PAR/inex using own HP Intranet login credentials
File Shares (Windows only):
    \\depot.nld.hp.com\depot\storage\3PAR. Using own HP Intranet login credentials. Go to iNex directory. iNex uses this file share for users within the EMEA domain.
    \\alffiles.alf.gsc.mvlabs.corp.hp.com\library\storage\3par. Using own HP Intranet login credentials. Go to iNex directory. iNex uses this file share for users within the AMERICAS domain.
    \\bglfiles.bgl.gsc.mvlabs.corp.hp.com\library\storage\3par. Using own HP Intranet login credentials. Go to iNex directory. iNex uses this file share for users within the ASIAPACIFIC domain.
All access is Read-Only.
NOTE: Replication from EMEA-based to non EMEA-based servers occurs during the weekend
Notes: There have been bugs in previous versions, forcing users to manually download updates.
With V1.22-1 these problems should be over (fingers crossed).
In V1.23-0 iNex will allow users to pre-define a drive letter to this network share and
Permanently connect it. In such case, iNex will use the existing drive letter.

## Slide 92: Auto_update: how it really (not) works
Example of a V1.22-1 <INEX_HOME>\log\auto_update.log
28-Aug-2014:08:21:25 1 Auto Update Utility of 3Par InSplore Explorer V1.22-1 31-Aug-2014 started at 28-Aug-2014:08:21:25
28-Aug-2014:08:21:25 3 Architecture: MSWin32-x86-multi-thread
28-Aug-2014:08:21:25 3 Running 32-bit version
28-Aug-2014:08:21:26 3 System has IP address 192.168.127.1 -> External
28-Aug-2014:08:21:26 3 System has IP address 192.168.76.1 -> External
28-Aug-2014:08:21:26 3 System has IP address 192.168.205.1 -> External
28-Aug-2014:08:21:26 3 System has IP address 192.168.1.69 -> External
28-Aug-2014:08:21:26 3 System has IP address 16.29.145.40 -> Internal
28-Aug-2014:08:21:26 3 Started from system 'VANSLUISH1.emea.hpqcorp.net' (IP: 16.29.145.40, Internal network) under account 'EMEA\vanSluisH'
28-Aug-2014:08:21:26 2 Drive Y: used to connect to '\\depot.nld.hp.com\depot\storage\3par‘ Creating network drive took 0 seconds.
28-Aug-2014:08:21:26 3 Connected from server depot.nld.hp.com
28-Aug-2014:08:21:26 3 Current Working Directory is now Y:\iNex\.
28-Aug-2014:08:21:26 3 Current Working Directory is now Y:\iNex\Windows
28-Aug-2014:08:21:26 3 No version newer than V1.22-1 found today. Will re-try tomorrow
28-Aug-2014:08:21:26 2 Drive Y: disconnected from '\\depot.nld.hp.com'
28-Aug-2014:08:21:26 0 ---------- E N D O F L O G F I L E ---------
Notes: V1.23-0 auto_update log file:
19-Oct-2014:14:32:48 1 Auto Update Utility of 3Par InSplore Explorer V1.23-0 31-Oct-2014 started at 19-Oct-2014:14:32:48
19-Oct-2014:14:32:48 3 Architecture: MSWin32-x86-multi-thread
19-Oct-2014:14:32:48 3 Running 32-bit version
19-Oct-2014:14:32:48 3 System has IP address 192.168.127.1 -> External
19-Oct-2014:14:32:48 3 System has IP address 192.168.76.1 -> External
19-Oct-2014:14:32:48 3 System has IP address 192.168.205.1 -> External
19-Oct-2014:14:32:48 3 System has IP address 192.168.1.70 -> External
19-Oct-2014:14:32:48 3 System has IP address 16.29.2.97 -> Internal
19-Oct-2014:14:32:48 3 Started from system 'VANSLUISH1.emea.hpqcorp.net' (IP: 16.29.2.97, Internal network) under account 'EMEA\vanSluisH'
19-Oct-2014:14:32:48 3 Drive letters currently in use:
19-Oct-2014:14:32:48 3 Drive C:\ Name: System FileSystem Type: (NTFS)
19-Oct-2014:14:32:48 3 Drive D:\ Name: Data1 FileSystem Type: (NTFS)
19-Oct-2014:14:32:48 3 Drive E:\ Name: Data2 FileSystem Type: (NTFS)
19-Oct-2014:14:32:48 3 Drive W:\ Name: InForm_Adm_Tools FileSystem Type: (CDFS)
19-Oct-2014:14:32:48 3 Attempt to use 'Z:' failed. Reason: OLE exception from "WSHNetwork.MapNetworkDrive": The local device name has a remembered connection to another network resource. Win32::OLE(0.1709) error 0x800704b2: "The local device name has a remembered connection to another network resource" in METHOD/PROPERTYGET "MapNetworkDrive"
19-Oct-2014:14:32:51 2 Drive Y: used to connect to '\\depot.nld.hp.com\depot\storage\3par'
19-Oct-2014:14:32:51 3 Connected from server depot.nld.hp.com
19-Oct-2014:14:32:52 3 Current Working Directory is now Y:\iNex\.
19-Oct-2014:14:32:52 3 Current Working Directory is now Y:\iNex\Windows
19-Oct-2014:14:32:52 3 New Patch 1 for version V122 detected
19-Oct-2014:14:33:52 3 Downloaded remote file "Y:\iNex\Windows\V122_iNex_Patch1.zip" as local file "D:\Products\3Par\Perl\Inex\V122_iNex_Patch1.zip"
19-Oct-2014:14:33:52 2 Drive Y: disconnected from '\\depot.nld.hp.com\/depot/storage/3par'
19-Oct-2014:14:33:52 3 Disconnected from server depot.nld.hp.com
19-Oct-2014:14:33:57 3 Start Job: /C D:\Products\3Par\Perl\Inex\bat\inex_change_version "V1.22-1" "D:\Products\3Par\Perl\Inex\V122_iNex_Patch1.zip"
19-Oct-2014:14:34:01 2 Process created and job is running: /C D:\Products\3Par\Perl\Inex\bat\inex_change_version "V1.22-1" "D:\Products\3Par\Perl\Inex\V122_iNex_Patch1.zip"
19-Oct-2014:14:34:01 0 ---------- E N D O F L O G F I L E ----------

## Slide 93: 3PAR Virtualization Mapping information, the MS-Access database

## Slide 94: iNex Virtualization Mapping Information
The MS-Access database
iNex supplies a skeleton database, enables loading the mapping information into a relational database.
Database is pre-loaded with Visual Basic forms and scripts.
Processing flow:
    Mapping information is automatically generated, in CSV format.
    Skeleton database is automatically copied to InSplore directory.
    In case mapping information is required, user can use form-driven procedure to load data.
Used by “find_remote_chunklets”, potential for other scripts.
Available in Windows version only.
Notes: The time to bulk load the database depends on the size of the configuration. Usually 30 – 45 seconds.

## Slide 95: iNex Virtualization Mapping Information
The MS-Access database (Main Form)
Upon opening database will be empty and “Load DB” button will be enabled.
After loading the database, the “Load DB” button will be disabled, and “VV to LD”, “LD to VV,PD” and “PD to LD” buttons will be enabled.

## Slide 96: iNex Virtualization Mapping Information
The MS-Access database (VV  LD Mapping)
List of LDs per VV space (adm/snp/usr)
VV areas mapped
on selected LD
All VV areas sorted
per VV space
and offset

## Slide 97: iNex Virtualization Mapping Information
The MS-Access database (LD  PD and LD  LD Mapping)
List of PDs used by selected LD
List of VVs mapped on selected LD

## Slide 98: iNex Virtualization Mapping Information
The MS-Access database (PD  LD Mapping)
Sequential list of used chunklets on selected PD
List of LDs mapped on selected PD

## Slide 99: iNex Virtualization Mapping Information
Find (and fix) remote chunklets
Utility to find (and fix) remote chunklets
    Remote chunklets are LD chunklets, not mapped on PD owned by LD owning node.
    Utility finds all remote chunklets by retrieving information from MS-Access database.
    Utility generates Unix shell script to move chunklets to PDs owned by LD owning node.
      Uses “movech –perm”
      Script will be placed in directory containing MS-Access database.
    Utility can be started from command line or GUI (Tools  “Find remote chunklets”)
Notes: If you use the GUI, then assure you first load in InSplore into iNex. After that, the Tools menu will be enabled.

## Slide 100: Customer Found Issue (CFI) database inter-action

## Slide 101: Customer Found Issue (CFI) database inter-action
Introduction
iNex has ability to automatically update existing CFI with SI / GR8 case numbers.
    The SI / GR8 case number must be specified.
      Manual entry into iNex the GUI or CLI
      Automatic entry into iNex if SI / GR8 case number is contained in directory name containing InSplore / evtlog / etc
    iNex encounters evidence during processing that InServ is exposed to known CFI
      Based upon information in analysis codes in <INEX_HOME>\defs\analysis_definitions.txt
      Will appear in Analysis Overview section on Overview worksheet
iNex has ability to automatically download copy of CFI and Crash footprint database.
    Allows for local reference of existing CFIs and node crash footprints, including BugZilla, SI / GR8 case and CFI numbers.
    Local references stored in SQLite database (<INEX_HOME>\databases\cfi.db). Ability for read-only access via Microsoft Excel .
    Right now: manual lookup of node crash via MS Excel
    Under Development: automatic lookup of node crash footprint, including confidence level, reference to Bugzilla, SI / GR8 case and CFI numbers.
    Local reference is updated once / day

## Slide 102: Customer Found Issue (CFI) database inter-action
High level data flow
Central CFI
Database
CFI Table
crashtxt
Local CFI db
Upload CFI db
Local workstation
cfi_upload
get_cfidb
get_cfidb
nightly scripts
Crash Table
STaTS
crashtxt

## Slide 103: Customer Found Issue (CFI) database inter-action
Automatic upload of CFI numbers to central CFI database
29-Aug-2014:16:53:50 1 3Par InSplore Explorer V1.22-0 15-Aug-2014 started at 29-Aug-2014:16:53:50
29-Aug-2014:16:53:50 1 Home directory detected as 'D:\Products\3Par\Perl\Inex'
29-Aug-2014:16:53:51 3 Found version 1. Expected version: 1. Database: 'cfiupload.db'
29-Aug-2014:16:53:51 3 Database 'cfiupload.db' successfully opened
29-Aug-2014:16:53:52 3 Connected to remote CFI database
29-Aug-2014:16:53:52 3 Case queue in database 'cfiupload.db' read (1 cases)
29-Aug-2014:16:53:52 3 Nr of Cases in queue: 1
29-Aug-2014:16:53:53 3 Case SIE58358 with CFI 3129 added to remote CFI database
29-Aug-2014:16:53:53 3 Case SIE58358 with CFI 3129 (SN: 1203125) successfully removed from database 'cfiupload.db'
29-Aug-2014:16:53:53 3 Database 'cfiupload.db' closed
29-Aug-2014:16:53:53 3 Disconnected from remote CFI database
29-Aug-2014:16:53:53 0 ---------- E N D O F L O G F I L E ----------
Notes: See <INEX_HOME>\log\cfi_upload.log

## Slide 104: Customer Found Issue (CFI) database inter-action
Automatic download of CFIs and crash footprints (logfile)
29-Aug-2014:19:43:22 1 3Par Get CFI Database Utility V1.22-1 31-Aug-2014 started at 29-Aug-2014:19:43:22
29-Aug-2014:19:43:22 1 Home directory detected as 'D:\Products\3Par\Perl\Inex'
29-Aug-2014:19:43:22 3 System has IP address 192.168.127.1 -> External
29-Aug-2014:19:43:22 3 System has IP address 192.168.76.1 -> External
29-Aug-2014:19:43:22 3 System has IP address 192.168.205.1 -> External
29-Aug-2014:19:43:22 3 System has IP address 192.168.1.69 -> External
29-Aug-2014:19:43:22 3 System has IP address 16.29.145.82 -> Internal
29-Aug-2014:19:43:22 3 Started from server 'VANSLUISH1.emea.hpqcorp.net' (IP: 16.29.145.82, Internal network) under account 'EMEA\vanSluisH'
29-Aug-2014:19:43:24 3 Connected to database 'cfisql'
29-Aug-2014:19:44:01 3 Remote CFI database closed
29-Aug-2014:19:44:02 3 Connected to remote stats database 'stats_config'
29-Aug-2014:19:44:10 3 Remote stats database closed
29-Aug-2014:19:44:10 3 Table INEX_DATABASE created successfully
29-Aug-2014:19:44:10 3 Table INEX_DATABASE updated successfully
29-Aug-2014:19:44:10 3 File 'D:\Products\3Par\Perl\Inex\databases\cfi.db' successfully created
29-Aug-2014:19:44:10 3 Found version 1. Expected version: 1. Database: 'cfi.db'
29-Aug-2014:19:44:10 3 Database 'cfi.db' successfully opened
29-Aug-2014:19:44:59 3 Database 'cfi.db' closed
29-Aug-2014:19:44:59 0 ---------- E N D O F L O G F I L E ---------
Notes: See <INEX_HOME>\log\get_cfgdb.log

## Slide 105: Customer Found Issue (CFI) database inter-action
Automatic download of CFIs and crash footprints (spreadsheet)
The local references are stored in SQLite database in <INEX_HOME>\databases\cfi.db
    After every run of iNex it will check if timestamp of database is > 24 hours ago.
      If so, a fresh copy will be downloaded
      If not, try next time.
    Requires connection to HP Intranet.
    Local reference contains CFIs of the following product families:
      3PAR StoreServ HW
      3PAR StoreServ SW
      HDD
Can be used as “External Data” within Microsoft Excel.
    Instructions on how to create are provided in “iNex Usage Guide”, chapter 8.
    32-bit and 64-bit DSNs provided with iNex installation kit. <INEX_HOME>\DSNs\...
  The quality of the CFI data is 100% dependent on the data entered by 3PAR ERT.

## Slide 106: Customer Found Issue (CFI) database inter-action
Requirements for CFI entry by 3PAR ERT team
Raise a CFI
In case of node crashes:
    Have the crashtxt file included as a whole in “Supporting Data” as Best Practice.
    At a minimum:
      The “Corefile Summary” section.
      The “Log Buffer Dump” section.
      The “Stack Trace Of Failing Task” section.
Put in BugZilla and SIE case numbers

## Slide 107: Customer Found Issue (CFI) database inter-action
Automatic download of CFIs and crash footprints (spreadsheet)
Microsoft Excel CFI spreadsheet
Typically created in same directory as local reference, so <INEX_HOME>\databases
Shortcut placed on Desktop for easy access
8 Possible Worksheets:
  3PAR CFIs
  HDD CFIs
  3PAR StackTraces
  3PAR BackTraces
  3PAR ERT Cases
  3PAR BugZilla numbers
  TPD Version Name  Numbers
  CFIs related to InFormOS upgrades
    Data can be automatically refreshed. See http://office.microsoft.com/en-us/excel-help/refresh-connected-imported-data-HP010342826.aspx

## Slide 108: Customer Found Issue (CFI) database inter-action
Node Crash Footprint recognition
Based upon the availability of several pieces of information:
  Panic string
  Stack Trace
  Back Trace
Method used is to copy and paste panic string, stack trace and optional back trace into dedicated tab of iNex GUI.
  By reading crashtxt file into text editor.
    Available on STaTS
  By reading analysis.<number> file into text editor
    Part of crashdmp as available on STaTS
    On actual node, located in /var/core/kernel/<numberX>/analysis.<numberY>
Best practice is to copy and paste complete crashtxt / analysis.<number> file into iNex GUI

## Slide 109: Customer Found Issue (CFI) database inter-action
Node Crash Footprint recognition
Copy and Paste crashtxt file contents into here
Analysis output will appear here

## Slide 110: Customer Found Issue (CFI) database inter-action
Node Crash Footprint recognition

## Slide 111: Customer Found Issue (CFI) database inter-action
Node Crash Footprint recognition
Appears after clicking on match line in previous window
CFI tab displays information about CFI:
WorkAround,
Supporting Data,
Observed Cases,
Version Info
Resolution
Title
Description
CFI tab contains hyperlink to BugZilla

## Slide 112: Customer Found Issue (CFI) database inter-action
Node Crash Footprint recognition
Confidence level
Experienced Panic string and stack trace
Compare to Panic string and stack trace
CFI information, Observed cases (including hyperlinks)
Notes: File is located in the following location:
<CustomersDirectory>\1_NodePanics\<SystemSerialNr>\NodePanic_<SystemSerialNr>_n<node>_<datetime>.xlsm
Example:
D:\Customers\1_NodePanics\1645457\NodePanic_1645457_n0_20141016204224.xlsm
Which contains the node crash information of system 1645457, node0 of 16-Oct-2014 20:42:24
The confidence level will be listed in descending order, so highest one first. Note that the example
shows a 100% hit. The databar will be adjusted accordingly.

## Slide 113: Questions ? Demo ?

## Slide 114: Thank you