## Slide 1: Disk Alignment
File System Partitions on Storage Devices

## Slide 2: Overview
The following slides show an example of how miss-alignment between a file system partition and a physical drive can occur and what the consequences can be
By no means it suggests that this misalignment applies to all possible combinations of OS/File System types and disk drives
It is just a basic explanation of how overhead can occur because of this and how re-alignment can reduce this overhead and for that reason improve performance

## Slide 3: Misalignment between File System Partition and HDD
0 |  |  |  |  | 63 | 64 |  |  |  |  | 127 | 128 | 
Sector
Block
Ext
Int
1 |  |  |  | 63 | 1 |  |  |  | 63 | 1 |  |  | 
MBR
Track 1
Track 2
Track 3
Track 1
Track 2
Disk drive reported to OS with 63 sectors per track (External)
Partitions must be on track boundary, 1st partition starts on track2/sector1
HDD layout (Internal) is different and uses logical blocks, 64 blocks per track
This is a track boundary misalignment when writing multiples of 64 bytes, e.g. 4KB
A physical drive can have hundreds of sectors per track; in this example 128
Start of 1st Partition
(before alignment)
Start of 1st Partition
(after alignment)
Or here…

## Slide 4: Re-alignment Tools for Windows
Tools (Microsoft)
  diskpar.exe (blocks)
  diskpart.exe1 (KBs)
Can improve performance by removing cache processing overhead
  E.g. look at: "Recommendations for Aligning VMFS Partitions" by VMware
1 as from W2K3 SP1

## Slide 5: Zoned Bit Recording
Moderns hard disks do not have a fixed number of sectors per track; different zones have a different number of sectors
Drives report 63 sectors/track:  external geometry
A drive can have hundreds of sectors per track
Internally Logical Block Addressing is used:  internal geometry
Because of this, re-alignment may not be straightforward and requires benchmark testing; e.g. Jetstress tool for Microsoft Exchange