## Slide 1: Chapter 12: Advanced BGP
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 12 Content
This chapter covers the following content:
Route Summarization - This section provides an overview of the how route summarization works with Border Gateway Protocol (BGP) and some design considerations related to summarization.
BGP Route Filtering and Manipulation - This section demonstrates the filtering and manipulation of routes based on network prefix, AS_Path, or other BGP path attributes.
BGP Communities - This section explains BGP communities and how the well-known communities influence prefix advertisements along with how they are used for conditional prefix filtering or manipulation.
Maximum Prefix - This section explains how a router can limit the number of prefixes received to ensure that the BGP table does not exceed its capacity.
Configuration Scalability - This section explains the use of peer groups and peer templates to assist with BGP configurations on routers with a lot of BGP sessions.

## Slide 3: Route Summarization
Summarizing prefixes conserves router resources and accelerates best-path calculation by reducing the size of the table.
Summarization also provides the benefit of stability by hiding route flaps from downstream routers, thereby reducing routing churn.
Route summarization can reduce the size of the BGP table for Internet routers.

## Slide 4: Route Summarization Aggregate Addresses
Dynamic BGP summarization consists of the configuration of an aggregate network prefix. When viable component routes that match the aggregate network prefix enter the BGP table, the aggregate prefix is created. The originating router sets the next hop to Null0 as a discard route for the aggregated prefix for loop prevention.
Dynamic route summarization is accomplished with the BGP address family configuration command aggregate-address network subnet-mask [summary-only] [as-set].
Figure 12-1 shows a simple topology in which R1 established an External BGP (eBGP) session with R2, and R2 establishes an eBGP session with R3.

## Slide 5: Route Summarization Route Aggregation
Example 12-1 demonstrates the BGP tables before route aggregation has been performed for R1.
Example 12-2 shows the route aggregation configuration for R1 & R2.
Example 12-3 shows the BGP tables on R1, after aggregation is configured.

## Slide 6: Route Summarization Route Aggregation Configuration with Suppression
The aggregate-address command advertises the aggregated network prefix in addition to the original component network prefixes. The optional summary-only keyword suppresses the component network prefixes in the summarized network prefix range.
Example 12-4 demonstrates the configuration with the summary-only keyword.
Example 12-5 shows the BGP table for R3 after the summary-only keyword is added to the aggregation command.

## Slide 7: Route Summarization Verify Route Aggregation with Suppression
Example 12-6 shows the BGP table and the Routing Information Base (RIB) for R2.
Example 12-7 shows that R1’s stub networks are suppressed, and the summary discard route for the 172.16.0.0/20 is installed in the RIB as well.

## Slide 8: Route Summarization The Atomic Aggregate Attribute
When a BGP router summarizes a route, it does not advertise the AS_Path information from before the aggregation. The atomic aggregate attribute indicates that a loss of path information has occurred.
Example 12-10 shows R3’s BGP entry for the 172.16.0.0/20 network prefix.
The route’s NLRI information indicates that the routes were aggregated by AS 65200 by the router with the router ID (RID) 192.168.2.2.
In addition, the atomic aggregate attribute has been set to indicate a loss of path attributes such as AS_Path in this scenario.

## Slide 9: Route Summarization Route Aggregation with AS_SET
To keep the BGP path information history, the optional as-set keyword may be used with the aggregate-address command. As the router generates the aggregate route, BGP attributes from the component aggregate routes are copied over to it.
The AS_Path settings from the original prefixes are stored in the AS_SET portion of AS_Path. AS_SET, which is displayed within brackets, counts as only one AS hop, even if multiple ASs are listed.
Example 12-11 shows R2’s updated BGP configuration for summarizing both prefixes with the as-set keyword.

## Slide 10: Route Summarization Verifying Path Attributes and Aggregated Properties
Example 12-12 shows the 172.16.0.0/20 network prefix again, now that BGP attributes are to be propagated into the new prefix. Notice that the AS_Path information now contains AS 65100.
Example 12-13 displays R2’s BGP table and the path attributes for the aggregated
192.168.0.0/16 network entry.

## Slide 11: Route Summarization Route Aggregation with AS_SET
R1 does not install the 192.168.0.0/16 network prefix for the same reason that R3 does not
install the 192.168.0.0/16 network prefix. R1 thinks that the advertisement is a loop because
it detects AS 65100 in AS_Path. You can confirm this by examining R1’s BGP table, shown in
Example 12-14.

## Slide 12: BGP Route Filtering and Manipulation
Conditional route selection is a method for selectively identifying prefixes that are advertised or received from peers.
Selected routes can be modified or removed to manipulate traffic flows, reduce memory utilization, or improve security.

## Slide 13: BGP Route Filtering and Manipulation BGP Route Filtering and Manipulation
Figure 12-2 shows the complete BGP route processing logic. Notice that the route policies
occur on inbound route receipt and outbound route advertisement.

## Slide 14: BGP Route Filtering and Manipulation BGP Route Filtering and Manipulation (Cont.)
IOS XE provides four methods of filtering routes inbound or outbound for a specific BGP
peer. Each of these methods can be used individually or simultaneously with other methods:
Distribution list - A distribution list filters network prefixes based on a standard or extended access control list (ACL). An implicit deny is associated with any prefix that is not permitted.
Prefix list - A list of prefix-matching specifications that permit or deny network prefixes in a top-down fashion, much like an ACL. An implicit deny is associated with any prefix that is not permitted.
AS_Path ACL/filtering - A list of regex commands that allows for the permit or deny of a network prefix, based on the current AS_Path values. An implicit deny is associated with any prefix that is not permitted.
Route maps - Route maps provide a method of conditional matching on a variety of prefix attributes and allow you to take a variety of actions. An action could be a simple permit or deny or could include the modification of BGP path attributes. An implicit deny is associated with any prefix that is not permitted.

## Slide 15: BGP Route Filtering and Manipulation Distribution List Filtering
Distribution lists allow the filtering of network prefixes on a neighbor-by-neighbor basis,
using standard or extended ACLs. To configure a distribute list, you use the BGP address
family configuration command neighbor ip-address distribute-list {acl-number | acl-name}
{in | out}.
Example 12-16 shows R1’s BGP configuration, which demonstrates filtering with distribution lists.
Example 12-17 shows the routing table of R1.

## Slide 16: BGP Route Filtering and Manipulation Prefix List Filtering
Prefix lists allow the filtering of network prefixes on a neighbor-by-neighbor basis, using
a prefix list. Configuring a prefix list involves using the BGP address family configuration
command neighbor ip-address prefix-list prefix-list-name {in | out}.
Example 12-18 shows the configuration of the prefix list and application to R2.
Example 12-19 shows the prefix list has been applied on R1.

## Slide 17: BGP Route Filtering and Manipulation AS_Path Filtering
There may be times when conditionally matching network prefixes may be too complicated,
and identifying all routes from a specific organization is preferred. In such a case, path
selection can be used with the BGP AS_Path. AS_Path filtering is accomplished using an
AS_Path ACL, which uses regular expressions for matching.
To parse through the large number of available ASNs (4,294,967,295), you can use regular expressions (regex).
Table 12-2 provides a brief list and description of the common regex query modifiers.

## Slide 18: BGP Route Filtering and Manipulation BGP Table for Regex Queries
The BGP table can be parsed with regex using the command show bgp afi safi regexp regex-pattern.
Figure 12-3 provides a reference topology, and Example 12-20 shows a reference BGP table to demonstrate the various regex query modifiers that can be used for a variety of common tasks.
AS_Path for the prefix 172.16.129.0/24 includes AS 300 twice non-consecutively for a specific purpose. This would not be seen in real life because it indicates a routing loop.

## Slide 19: BGP Route Filtering and Manipulation BGP Regex Queries
Example 12-22 shows how to use the underscore (_) to imply a space left of the ASN (100) remove the unwanted ASNs. The regex query includes the following unwanted ASN: 10010.
Example 12-25 shows the caret (^) in the regex pattern.
Example 12-27 provides a solution using the dollar sign ($) for the regex the pattern _40$.

## Slide 20: BGP Route Filtering and Manipulation AS_Path ACLs
Selecting routes from a BGP neighbor by using AS_Path requires the definition of an AS_Path access control list (AS_Path ACL). The AS_Path ACL processing is performed in a sequential top-down order, and the first qualifying match processes against the appropriate permit or deny action. An implicit deny exists at the end of the AS path ACL.
The command ip as-path access-list acl-number {deny | permit} regex-query creates the AS_Path access-list. The ACL is then applied with the command neighbor ip-address filter-list acl-number {in | out}.
Example 12-37 shows the configuration on R2 using an AS_Path ACL to restrict traffic to only locally originated traffic using the regex pattern ^$. To ensure completeness, the AS_Path ACL is applied on all eBGP neighborships.

## Slide 21: BGP Route Filtering and Manipulation AS_Path ACLs (Cont.)
Example 12-36 shows the routes before the BGP AS_Path ACL was applied.
Example 12-38 shows the routes being advertised to R1. Notice that the routes
do not all have AS_Paths confirming that only locally originating routes are being advertised externally.

## Slide 22: BGP Route Filtering and Manipulation Route Maps
Route maps provide more functionality than pure filtering; they provide a method to manipulate BGP path attributes as well.
Route maps are applied on a BGP neighbor basis for routes that are advertised or received. A different route map can be used for each direction.
The route map is associated to the BGP neighbor with the command neighbor ip-address route-map route-map-name {in | out} under the specific address family.
Route maps allow for multiple steps in processing as well.

## Slide 23: BGP Route Filtering and Manipulation Route Map Configuration
Example 12-40 shows R1’s configuration, where multiple prefix lists are referenced along
with an AS_Path ACL.
This route map includes four steps:
Step 1. Deny any routes that are in the 192.168.0.0/16 network by using a prefix list.
Step 2. Match any routes originating from AS 65200 and are within the 100.64.0.0/10 network range and set the BGP local preference to 222.
Step 3. Match any routes originating from AS 65200 that did not match step 2 and set the BGP weight to 65200.
Step 4. Permit all other routes to process.

## Slide 24: BGP Route Filtering and Manipulation Verifying Route Map
Example 12-39 shows R1’s BGP routing table before a route map was applied and Example 12-41 shows after the route map was applied. The following actions occurred:
The 192.168.2.2/32 and 192.168.3.3/32 routes were discarded. The 192.168.1.1/32 route is a locally generated route.
The 100.64.2.0/25 and 100.64.2.192/26 networks had the local preference modified to 222 because they originate from AS 65200 and are within the 100.64.0.0/10 network range.
The 10.12.1.0/24 and 10.23.1.0/24 routes from R2 have been assigned the locally significant BGP attribute weight 65200.
All other routes were received and not modified.

## Slide 25: BGP Route Filtering and Manipulation Clearing BGP Connections
Depending on the change to the BGP route manipulation technique, the BGP session may need to be refreshed to take effect. BGP supports two methods of clearing a BGP session.
The first method is a hard reset, which tears down the BGP session, removes BGP routes from the peer, and is the most disruptive.
    You can initiate a hard reset on a router with the command clear ip bgp ip-address. You can clear all the router’s BGP sessions by using an asterisk (*) in lieu of the peer’s IP address.
The second method is a soft reset, which invalidates the BGP cache and requests a full advertisement from its BGP peer. A soft reset reduces the number of routes that must be exchanged if multiple address families are configured with a single BGP peer.
    You can initiate a soft reset on a router with the command clear ip bgp ip-address soft
    You can perform a soft reset for a specific address family with the command clear bgp afi safi {ip-address | *} soft [in | out].

## Slide 26: BGP Communities
BGP communities provide additional capability for tagging routes and for modifying BGP routing policy on upstream and downstream routers.
BGP communities can be appended, removed, or modified selectively on each attribute from router to router.

## Slide 27: BGP Communities BGP Communities
BGP communities are an optional transitive BGP attribute that can traverse from AS to AS. A BGP community is a 32-bit number that can be included with a route. A BGP community can be displayed as a full 32-bit number (0 through 4,294,967,295) or as two 16-bit numbers (0 through 65535):(0 through 65535), commonly referred to as new format.
By convention, with private BGP communities, the first 16 bits represent the AS of the community origination, and the second 16 bits represent a pattern defined by the originating AS.
The private BGP community pattern can vary from organization to organization and does not need to be registered. The pattern could signify geographic locations for one AS while signifying a method of route advertisement in another AS.
In 2006, RFC 4360 expanded the capabilities of BGP communities by providing an extended format. Extended BGP communities provide structure for various classes of information and are commonly used for VPN services.

## Slide 28: BGP Communities Enabling BGP Community Support
IOS and IOS XE routers do not advertise BGP communities to peers by default. Communities are enabled on a neighbor-by-neighbor basis with the BGP address family configuration command neighbor ip-address send-community [standard | extended | both] under the neighbor’s address family configuration.
If a keyword is not specified, standard communities are sent by default.
IOS XE nodes can display communities in new format, and they are easier to read if you use the global configuration command ip bgp-community new-format.
Example 12-42 shows the BGP community in decimal format on top and then in new format.

## Slide 29: BGP Communities Well-Known Communities
RFC 1997 defined a set of global communities (known as well-known communities) that use the community range 4,294,901,760 (0xFFFF0000) to 4,294,967,295 (0xFFFFFFFF). All routers that are capable of sending/receiving BGP communities must implement well-known communities.
The following are the common well-known communities:
Internet
No_Advertise
No_Export
Local-AS

## Slide 30: BGP Communities No-Advertise BGP Community
No_Advertise community routes should not be advertised to any BGP peer. The No_Advertise BGP community can be advertised from an upstream BGP peer or locally with an inbound BGP policy. The No_Advertise community is set with the command set community no-advertise within a route map.
Figure 12-4 demonstrates that R1 is advertising the 10.1.1.0/24 network to R2.
Example 12-43 shows R2’s Network Layer Reachability Information (NLRI) for the 10.1.1.0/24 network prefix.
BGP routes that are set with the No_Advertise community are quickly seen with the command show bgp afi safi community no-advertise, as shown in Example 12-44.

## Slide 31: BGP Communities No-Export BGP Community
When a route is received with the No_Export community, the route is not advertised to any eBGP peer. The No_Export community is set with the command set community no-export within a route map.
Figure 12-5 shows a topology with three ASs.
Example 12-45 confirms that the prefix is not advertised to any eBGP peer.
The command show bgp afi safi community no-export shows all the BGP prefixes that contain the Local-AS community, as demonstrated in Example 12-46.

## Slide 32: BGP Communities No-Export SubConfed Community
With the No_Export_SubConfed community known as the Local-AS community, a route is not advertised outside the local AS. The Local- AS community is set with the command set community local-as within a route map.
Figure 12-6 shows a topology with three ASs.
Example 12-47 confirms that the prefix is not advertised outside local AS and that the prefix is not advertised to any peer.
The command show bgp afi safi community local-as shows all the BGP prefixes that contain the Local-AS community, as demonstrated in Example 12-48.
Figure 12-6 BGP Local-AS Community Topology

## Slide 33: BGP Communities Conditionally Matching BGP Communities
Conditionally matching BGP communities allows for selection of routes based on the BGP communities within the route’s path attributes so that selective processing can occur in route maps.
You display the entire BGP table by using the command show bgp afi safi detail and then manually select a route with a specific community. However, if the BGP community is known, you can display all the routes by using the command show bgp afi safi community community.
Example 12-49 shows the BGP table for R1, which has received multiple routes from R2 (AS 65200).
Example 12-50 shows the explicit path entry for the 10.23.1.0/24 network and all the BGP path attributes.

## Slide 34: BGP Communities Conditionally Matching BGP Communities (Cont.)
Conditionally matching requires the creation of a community list that shares a similar structure to an ACL, can be standard or expanded, and can be referenced by number or name.
The configuration syntax for a community list is ip community-list {1-500 | standard list-name | expanded list-name} {permit | deny} community-pattern. The community list is referenced in a route map with the command match community 1-500.
Example 12-51 demonstrates the creation of a BGP community list that matches on the community 333:333.
Example 12-52 shows the BGP table after the route map has been applied to the neighbor.

## Slide 35: BGP Communities Private BGP Communities
You set a private BGP community in a route map by using the command set community bgp-community [additive]. By default, when you set a community, any existing communities are overwritten, but you can preserve them by using the optional additive keyword.
Example 12-54 shows the configuration where the BGP community is set on the 10.23.1.0/24 network.
After the route map has been applied and the routes have been refreshed, the path attributes can be examined, as demonstrated in Example 12-55.

## Slide 36: Maximum Prefix
The BGP maximum prefix feature restricts the number of routes that are received from a BGP peer.
This feature ensures that the BGP table does not overwhelm the router by exceeding its memory or processing capability.
Prefix limits are typically set for BGP peers on low-end routers as a safety mechanism to ensure that they do not become overloaded.

## Slide 37: Maximum Prefix Maximum Prefix
The BGP maximum prefix feature restricts the number of routes that are received from a BGP peer. This feature ensures that the BGP table does not overwhelm the router by exceeding its memory or processing capability.
Routers can place prefix restrictions on a BGP neighbor by using the BGP address family configuration command neighbor ip-address maximum-prefix prefix-count [warning-percentage] [restart time] [warning-only].
When a peer advertises more routes than the maximum prefix count, the peer moves the neighbor to the idle (PfxCt) state in the finite-state machine (FSM), closes the BGP session, and sends out the appropriate syslog message. The BGP session is not automatically reestablished by default. If you want to restart the BGP session after a certain amount of time, you can use the optional keyword restart time.

## Slide 38: Maximum Prefix Maximum Prefix (Cont.)
A warning is not generated before the prefix limit is reached. By adding a warning percentage (set to 1 to 100) after the maximum prefix count, you can have a warning message sent when the percentage is exceeded. The maximum prefix behavior of closing the BGP session can be changed by using the optional keyword warning-only so that a warning message is generated instead. When the threshold has been reached, additional prefixes are discarded.
Example 12-56 shows the maximum prefix configuration.
Example 12-57 shows the 10.12.1.2 neighbor has exceeded the maximum prefix threshold and shut down the BGP session.

## Slide 39: Configuration Scalability
BGP configurations can become fairly large as features are configured or BGP sessions increase.
IOS-based operating systems provide methods to apply a similar configuration to multiple neighbors.
This simplifies the configuration from a deployment standpoint and makes the configuration easier to read.

## Slide 40: Configuration Scalability IOS Peer Groups
IOS peer groups simplify BGP configuration and reduce system resource use (CPU and memory) by grouping BGP peers together into BGP update groups.
BGP update groups enable a router to perform the outbound routing policy processing one time and then replicate the update to all the members (as opposed to performing the outbound routing policy processing for every router).
All peer group settings use the peer-groupname field in lieu of the ip-address field in the neighbor ip-address commands. All routers in the peer group are in the same update group and therefore must be of the same session type: internal (iBGP) or external (eBGP).

## Slide 41: Configuration Scalability Peer Group Configuration
A peer group is defined by using the command neighbor group-name peer-group in the global BGP configuration. All BGP parameters are configured using peer-group groupname in lieu of neighbor ip-address.
To link BGP peer IP addresses to the peer group use the command neighbor ip-address peer-group group-name. BGP neighbors cannot be activated by peer group name and must be activated for each address family by IP address.
Example 12-58 shows R1’s BGP configuration for peering with R2, R3, and R4.

## Slide 42: Configuration Scalability IOS Peer Templates
IOS BGP peer templates allow for a reusable pattern of settings that can be applied as needed in a hierarchical format through inheritance and nesting of templates. If a conflict exists between an inherited configuration and the invoking peer template, the invoking template preempts the inherited value.
There are two types of BGP peer templates:
Peer session - This type of template involves configuration settings specifically for the BGP session. You define peer session template settings with the BGP configuration command template peer-session template-name and then enter any BGP session related configuration commands.
Peer policy - This type of template involves configuration settings specifically for the address family policy. You define peer policy template settings with the BGP configuration command template peer-policy template-name and then enter any BGP address family–related configuration commands.

## Slide 43: Prepare for the Exam

## Slide 44: Prepare for the Exam Key Topics for Chapter 12
Description |  | 
Aggregate addresses | Prefix list filtering | The No_Export BGP community
Route aggregation with suppression | Regular expressions (regex) | The Local-AS No_Export_SubConfed_ BGP Community
The Atomic aggregate attribute | AS_Path ACLs | Community list configuration
Route aggregation with AS_SET | Route maps | Setting private BGP communities
BGP route policy processing | Clearing BGP connections | Maximum prefix
BGP filtering methods | Enabling BGP community support | IOS peer groups
Distribution list filtering | The No_Advertise BGP community | IOS peer templates

## Slide 45: Prepare for the Exam Key Terms for Chapter 12
Key Terms | 
access control list (ACL) | No_Advertise community
AS path | peer group
atomic aggregate | peer template
BGP community | prefix list
BGP multihoming | regular expressions
distribute list | route map
Local-AS community | transit routing
No_Export community | 

## Slide 46: Prepare for the Exam Command Reference for Chapter 12
Task | Command Syntax
Configure a BGP aggregate IPv4 prefix | aggregate-address network subnet-mask [summary-only] [as-set]
Configure a BGP aggregate IPv6 prefix | aggregate-address prefix/prefixlength [summary-only] [as-set]
Configure a prefix list | {ip ¦ ipv6} prefix-list prefix-list-name [seq sequence-number] {permit ¦ deny} high-order-bit-pattern/ high-order-bit-count [ge ge-value] [le le-value]
Create a route map entry | route-map route-map-name [permit ¦ deny] [sequence-number]
Conditionally match in a route map using AS_Path | match as-path acl-number
Conditionally match in a route map using an ACL | match ip address {acl-number ¦ acl-name}
Conditionally match in a route map using a prefix list | match ip address prefix-list prefix-list-name

## Slide 47: Prepare for the Exam Command Reference for Chapter 12
Task | Command Syntax
Conditionally match in a route map using local preference | match local-preference local-preference
Filter routes to a BGP neighbor using an ACL | neighbor ip-address distribute-list {acl-number ¦ acl-name} {in ¦ out}
Filter routes to a BGP neighbor using a prefix list | neighbor ip-address prefix-list prefix-list-name {in ¦ out}
Create an ACL based on the BGP AS_Path | ip as-path access-list acl-number {deny ¦ permit} regex-query
Filter routes to a BGP neighbor using an AS_Path ACL | neighbor ip-address filter-list acl-number {in ¦ out}
Associate an inbound or outbound route map to a specific BGP neighbor | neighbor ip-address route-map route-map-name {in ¦ out}
Configure IOS-based routers to display the community in new format for easier readability of BGP communities | ip bgp-community new-format

## Slide 48: Prepare for the Exam Command Reference for Chapter 12
Task | Command Syntax
Create a BGP community list for conditional route matching | ip community-list {1-500 ¦ standard list-name ¦ expanded list-name} {permit ¦ deny} community-pattern
Set BGP communities in a route map | set community bgp-community [additive]
Configure the maximum number of BGP prefixes that a neighbor can receive | neighbor ip-address maximum-prefix prefix-count [warning-percentage] [restart time] [warning-only]
Define a BGP peer group | neighbor group-name peer-group
Initiate a route refresh for a specific BGP peer | clear bgp afi safi {ip-address¦*} soft [in ¦ out].
Display the current BGP table, based on routes that meet a specified AS_Path regex pattern | show bgp afi safi regexp regex-pattern
Display the current BGP table, based on routes that meet a specified BGP community | show bgp afi safi community community