## Slide 1: Chapter 15: Route Maps and Conditional Forwarding
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 15 Content
This chapter covers the following content:
Conditional Matching - This section provides an overview of how network prefixes can be conditionally matched with ACLs or prefix lists.
Route Maps - This section explains the structure of a route map and how conditional matching and conditional actions can be combined to filter or manipulate routes.
Conditional Forwarding of Packets - This section explains how a router forwards packets down different paths based on the network traffic.
Trouble Tickets - This section provides three trouble tickets that demonstrate how a structured troubleshooting process can be used to solve a reported problem.

## Slide 3: Conditional Matching
Applying bulk changes to routes does not allow for easy tuning of the network.
This section reviews some of the common techniques used to conditionally match a route—using access control lists (ACLs) and prefix lists.

## Slide 4: Conditional Matching Access Control Lists (ACLs)
ACLs provide packet classification for a variety of features, such as quality of service (QoS), or for identifying networks within routing protocols.
ACLs are composed of access control entries (ACEs), which are entries in the ACL that identify the action to be taken (permit or deny) and the relevant packet classification.
Packet classification starts at the top (lowest sequence) and proceeds down (higher sequence) until a matching pattern is identified. When a match is found, the appropriate action (permit or deny) is taken, and processing stops.
At the end of every ACL is an implicit deny ACE, which denies all packets that did not match earlier in the ACL.

## Slide 5: Conditional Matching Access Control Lists (Cont.)
ACLs are classified into two categories:
Standard ACLs - Define packets based solely on the source network. Standard ACLS use a numbered entry 1–99 or 1300–1999 or a named ACL.
Extended ACLs - Define packets based on the source, destination, protocol, port, or a combination of other packet attributes. Extended ACLs use a numbered entry 100–199 or 2000–2699 or a named ACL.
Named ACLs provide relevance to the functionality of an ACL, can be used with standard or extended ACLs, and are generally preferred.
Note: ACE placement within an ACL is important, and unintended consequences may result from ACEs being out of order.

## Slide 6: Conditional Matching Standard ACLs
The process for defining a standard ACL is as follows:
Step 1. Define the ACL by using the command ip access-list standard {acl-number | acl-name} and placing the CLI in ACL configuration mode.
Step 2. Configure the specific ACE entry with the command [sequence] {permit | deny} source source-wildcard. In lieu of using source source-wildcard, the keyword any replaces 0.0.0.0 0.0.0.0, and use of the host keyword refers to a /32 IP address so that the source-wildcard can be omitted.
Table 15-2 provides sample ACL entries from within the ACL configuration mode and specifies the networks that would match with a standard ACL.

## Slide 7: Conditional Matching Extended ACLs
The process for defining an extended ACL is as follows:
Step 1. Define the ACL by using the command ip access-list extended {acl-number | acl-name} and placing the CLI in ACL configuration mode.
Step 2. Configure the specific ACE entry with the command [sequence] {permit | deny} protocol source source-wildcard destination destination-wildcard.
Table 15-3 provides sample ACL entries from within the ACL configuration mode and specifies the networks that would match with the extended ACL.

## Slide 8: Conditional Matching IGP Network Selection
When ACLS are used for IGP network selection, the source fields of the ACL are used to identify the network, and the destination fields identify the smallest prefix length allowed in the network range. Table 15-3 provides sample ACL entries from within the ACL configuration mode and specifies the networks that would match with the extended ACL.

## Slide 9: Conditional Matching BGP Network Selection
Extended ACLs react differently when matching BGP routes than when matching IGP routes.
The source fields match against the network portion of the route, and the destination fields
match against the network mask, as shown in Figure 15-1. Until the introduction of prefix
lists, extended ACLs were the only match criteria used with BGP.
Table 15-4 demonstrates the concept of the wildcard for the network mask and subnet mask.

## Slide 10: Conditional Matching Prefix Matching
Prefix lists provide another method of identifying networks in a routing protocol. A prefix list identifies a specific IP address, network, or network range and allows for the selection of multiple networks with a variety of prefix lengths, using a prefix match specification.
A prefix match specification contains two parts: a high-order bit pattern and a high-order bit count, which determines the high-order bits in the bit pattern that are to be matched. Some documentation refers to the high-order bit pattern as the address or network and the high-order bit count as the length or mask length.
In Figure 15-2, the prefix match specification has the high-order bit pattern 192.168.0.0 and the high-order bit count 16.

## Slide 11: Conditional Matching Prefix Matching (Cont.)
Figure 15-3 demonstrates the prefix match specification with a high-order bit pattern of 10.168.0.0 and high-order bit count of 13, where the matching length of the prefix must be greater than or equal to 24.
Figure 15-4 demonstrates a prefix match specification with a high order bit pattern of 10.0.0.0 and high-order bit count of 8, where the matching length must be between 22 and 26.

## Slide 12: Conditional Matching Prefix Lists
A prefix list can have multiple prefix matching specification entries that contain permit or deny actions. Prefix lists process in sequential order in a top-down fashion, and the first prefix match processes with the appropriate permit or deny action. Prefix lists are configured with the following global configuration command syntax:
ip prefix-list prefix-list-name [seq sequence-number] {permit | deny} high-order-bit-pattern/high-order-bit-count [ge ge-value] [le le-value]
If a sequence is not provided, the sequence number auto-increments by 5, based on the highest
sequence number. The first entry is 5. Example 15-1 provides a sample prefix list named RFC1918 for all the networks in the RFC 1918 address range.

## Slide 13: Conditional Matching IPv6 Prefix Lists
The prefix matching logic works exactly the same for IPv6 networks as for IPv4 networks.
The most important thing to remember is that IPv6 networks are notated in hex and not in binary when identifying ranges. IPv6 prefix lists are configured with the following global configuration command syntax:
ipv6 prefix-list prefix-list-name [seq sequence-number] {permit | deny} high-order-bit-pattern/high-order-bit-count [ge ge-value] [le le-value]
Example 15-2 provides a sample prefix list named PRIVATE-IPV6 for all the networks in the documentation and benchmarking IPv6 space.

## Slide 14: Route Maps
Route maps provide many different features to a variety of routing protocols.
At the simplest level, route maps can filter networks much the same way as ACLs, but they also provide additional capability through the addition or modification of network attributes.
To influence a routing protocol, a route map must be referenced from the routing protocol.

## Slide 15: Route Maps Route Maps
Route maps are critical to BGP because they are the main component in modifying a unique routing policy on a neighbor-by-neighbor basis. Route maps have four components:
Sequence number - Dictates the processing order of the route map.
Conditional matching criterion - Identifies prefix characteristics (network, BGP path attribute, next hop, and so on) for a specific sequence.
Processing action - Permits or denies the prefix.
Optional action - Allows for manipulations dependent on how the route map is referenced on the router. Actions can include modification, addition, or removal of route characteristics.

## Slide 16: Route Maps Route Map Configuration
A route map use the following command syntax: route-map route-map-name [permit | deny] [sequence-number]
The following rules apply to route-map statements:
If a processing action is not provided, the default value of permit is used.
If a sequence number is not provided, the sequence number increments by 10 automatically.
If a matching statement is not included, an implied all prefixes is associated with the statement.
Processing within a route map stops after all optional actions have been processed (if configured) after matching a matching criterion.
Example 15-3 provides a sample route map to demonstrate the four components of a route map.

## Slide 17: Route Maps Conditional Matching Commands
Table 15-5 provides the command syntax for the most common methods for conditionally matching prefixes and describes their usage

## Slide 18: Route Maps Multiple Conditional Match Conditions
If multiple variables (ACLs, prefix lists, tags, and so on) are configured for a specific route map sequence, only one variable must match for the prefix to qualify. The Boolean logic uses an or operator for this configuration. If multiple match options are configured for a specific route map sequence, both match options must be met for the prefix to qualify for that sequence. The Boolean logic uses an and operator for this configuration.
In Example 15-4, sequence 10 requires that a prefix pass ACL-ONE or ACL-TWO. Notice that sequence 20 does not have a match statement, so all prefixes that are not passed in sequence 10 qualify and are denied.
  route-map EXAMPLE permit 10
  match ip address ACL-ONE
  match metric 550 +- 50
In the above snippet, sequence 10 requires that the prefix match ACL ACL-ONE and that the metric be a value between 500 and 600.

## Slide 19: Route Maps Complex Matching
Some network engineers find route maps too complex if the conditional matching criteria
use an ACL, an AS_Path ACL, or a prefix list that contains a deny statement. Example 15-5
shows a configuration in which the ACL uses a deny statement for the 172.16.1.0/24 network
range.
Configurations should follow the sequence order first and conditional matching criteria second, and only after a match occurs should the processing action and optional action be used.
Matching a deny statement in the conditional match criteria excludes the route from that sequence in the route map.

## Slide 20: Route Maps Optional Actions
In addition to permitting a prefix to pass, a route map can modify route attributes. Table 15-6 provides a brief overview of the most popular attribute modifications.
Adding the keyword continue to a route map allows the route map to continue processing other route map sequences. Example 15-6 provides a basic configuration.

## Slide 21: Conditional Forwarding of Packets
A router makes forwarding decisions based on the destination addresses IP packets.
Some scenarios accommodate other factors, such as packet length or source address, when deciding where the router should forward a packet.

## Slide 22: Conditional Forwarding of Packets Policy-Based Routing (PBR)
Policy-based routing (PBR) allows for conditional forwarding of packets based on packet characteristics besides the destination IP address. PBR provides the following capabilities:
Routing by protocol type (ICMP, TCP, UDP, and so on)
Routing by source IP address, destination IP address, or both
Manual assignment of different network paths to the same destination, based on tolerance for latency, link speed, or utilization for specific transient traffic
Some of the drawbacks of conditional routing include the following:
Administrative burden in scalability
Lack of network intelligence
Troubleshooting complexity

## Slide 23: Conditional Forwarding of Packets PBR Configuration
PBR configuration uses a route map with match and set statements that are attached to the inbound interface. It involves the following steps:
Step 1. Configure the route map by using the command route-map route-map-name [permit | deny] [sequence-number].
Step 2. Identify the conditional match criteria. The conditional match criteria can be based on packet length with the command match length minimum-length maximum-length or can be based on the packet IP address fields with an ACL using the command match ip address {access-list-number | acl-name}.
Step 3. Use the command set ip [default] next-hop ip-address [... ip-address] to specify one or more next hops for packets that match the criteria. The optional default keyword changes the behavior so that the next-hop address specified by the route map is used only if the destination address does not exist in the RIB. If a viable route exists in the RIB, then that is the next-hop address that is used for forwarding the packet.
Step 4. Apply the route map to the inbound interface by using the interface parameter command ip policy route-map route-map-name.

## Slide 24: Conditional Forwarding of Packets PBR Configuration (Cont.)
Example 15-7 shows the normal traffic path using traceroute between the 10.1.1.0/24 and 10.5.5.0/24 networks without PBR configured.
Figure 15-5 provides a sample topology for illustrating PBR concepts. R1, R2, R3, R4, and R5 are all configured with OSPF.
Example 15-8 shows the PBR configuration on R2 for network traffic from 10.1.1.0/24 destined for the 10.5.5.0/24 network to route traffic to 10.23.1.3 (R3).

## Slide 25: Conditional Forwarding of Packets PBR Configuration (Cont.)
Example 15-9 shows the traffic path between the 10.1.1.0/24 and 10.5.5.0/24 networks after the conditional route forwarding policies are applied.
Example 15-10 shows that applying a PBR configuration does not modify the routing table.

## Slide 26: Conditional Forwarding of Packets Local PBR
Packets originated by the router are not policy routed. There is a feature for policy routing of locally generated traffic through local PBR. Local PBR policies are applied to the router with the global configuration command ip local policy route-map-name.
Figure 15-6 demonstrates a scenario where R1 is managed by an interface specifically for out-of-band management on the 172.16.14.0/24 network.

## Slide 27: Conditional Forwarding of Packets Local PBR Configuration
Example 15-11 demonstrates that R1 forwards traffic from its GigabitEthernet 0/2 interface through 10.12.1.0/24 to the network management system on the 10.33.33.0/24 network.
If you configure a local PBR on R1, it will only modify the next-hop IP address on traffic that is sourced locally from the 172.16.14.0/24 network by modifying the next-hop IP address to 172.16.14.4. Example 15-12 shows the local PBR configuration for R1.

## Slide 28: Conditional Forwarding of Packets Local PBR Verification
With the local PBR policy placed on R1, Example 15-13 verifies that network traffic
between 172.16.14.1 and 10.33.33.0/24 will use the out-of-band networks (172.16.0.0/16).
You can view policy-based decisions by enabling debugging functionality on policy-based routing with the command debug ip policy. Example 15-14 shows the use of the debug command and the initiation of traffic that matches the PBR to display the output.

## Slide 29: Trouble Tickets
This section presents various trouble tickets relating to the topics discussed in this chapter.
The purpose of trouble tickets is to show a process that you can follow when troubleshooting in the real world or in an exam environment.

## Slide 30: Trouble Tickets Trouble Ticket 15-1
Problem: Traffic from 10.1.4.0/24 to 10.1.1.0/24 is routed through R2 using Gi3/0, but it should be routed directly to R1 using Fa1/0. You begin troubleshooting by verifying the problem with a trace from a PC in 10.1.4.0/24 with the destination 10.1.1.1.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 31: Trouble Tickets Trouble Ticket 15-2
Problem: Traffic from 10.1.4.0/24 to 10.1.1.0/24 is routed though R2 using Gi3/0, but it should be routed directly to R1 using Fa1/0. You begin troubleshooting by verifying the problem with a trace from a PC in 10.1.4.0/24 (Branch) with the destination 10.1.1.1.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 32: Trouble Tickets Trouble Ticket 15-3
Problem: Traffic from 10.1.4.0/24 to 10.1.1.0/24 is routed though R2 using Gi3/0, but it should be routed directly to R1 using Fa1/0. You begin troubleshooting by verifying the problem with a trace from a PC in 10.1.4.0/24 with the destination 10.1.1.1.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 33: Prepare for the Exam

## Slide 34: Prepare for the Exam Key Topics for Chapter 15
Description | 
Access control lists (ACLs) | Route maps
Extended ACLs for IGP route selection | Conditional matching
Extended ACLs for BGP route selection | Multiple conditional match conditions
Prefix matching specification | Complex matching
Prefix match high-order bit pattern | Optional actions
Prefix match with length parameters | Policy-based routing (PBR)
Prefix lists | Local PBR
IPv6 prefix lists | 

## Slide 35: Prepare for the Exam Key Terms for Chapter 15
Key Terms
prefix list
policy-based routing
route map

## Slide 36: Prepare for the Exam Command Reference for Chapter 15
Task | Command Syntax
Configure a prefix list | {ip ¦ ipv6} prefix-list prefix-list-name [seq sequence-number] {permit ¦ deny} high-order-bit-pattern/high-order-bit-count [ge ge-value] [le le-value]
Create a route map entry | route-map route-map-name [permit ¦ deny] [sequence-number]
Conditionally match in a route map using AS_Path | match as-path acl-number
Conditionally match in a route map using an ACL | match ip address {acl-number ¦ acl-name}
Conditionally match in a route map using a prefix list | match ip address prefix-list prefix-list-name
Conditionally match in a route map using local preference | match local-preference local-preference

## Slide 37: Prepare for the Exam Command Reference for Chapter 15 (Cont.)
Task | Command Syntax
Prepend the AS_Path for the network prefix with the pattern specified or from multiple iterations from neighboring autonomous systems | set as-path prepend {as-number-pattern ¦ last-as 1-10}
Set the next-hop IP address for any matching prefix | set ip next-hop ip-address
Set the BGP PA local preference | set local-preference 0-4294967295
Set a numeric tag (0 through 4294967295) for identification of networks by other routers | set tag tag-value