## Slide 1: Chapter 8: Troubleshooting OSPFv2
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 8 Content
This chapter covers the following content:
Troubleshooting OSPFv2 Neighbor Adjacencies - This section covers the reasons OSPFv2 neighbor adjacencies sometimes do not form and how to identify them.
Troubleshooting OSPFv2 Routes - This section covers the reasons OSPFv2 routes might be missing from the link-state database (LSDB) and routing table and how to determine why they are missing.
Troubleshooting Miscellaneous OSPFv2 Issues - This section focuses on tracking link-state advertisements (LSAs) through the network, route summarization, discontiguous areas, load balancing, and default routes.
OSPFv2 Trouble Tickets - This section presents three trouble tickets that demonstrate how to use a structured troubleshooting process to solve a reported problem.

## Slide 3: Troubleshooting OSPFv2 Neighbor Adjacencies
This section focuses on the reasons an OSPF neighbor relationship might not form and how to identify them during the troubleshooting process.

## Slide 4: Troubleshooting OSPFv2 OSPF Establishes Neighbor Relationships
OSPF establishes neighbor relationships by sending hello packets out interfaces participating in the OSPF process. You can enable the OSPF process on an interface and place it in an OSPF area using two methods:
Router OSPF configuration mode.
R1(config)# router ospf 1 R1(config-router)# network 10.1.1.0 0.0.0.255 area 0
Interface configuration mode. R1(config)# interface g0/0 R1(config-if)# ip ospf 1 area 51

## Slide 5: Troubleshooting OSPFv2 Show IP OSPF Neighbor
To verify OSPFv2 neighbors, you use the show ip ospf neighbor command.
Example 8-1 shows sample output of the show ip ospf neighbor command. It lists:
Neighbor ID – The router ID (RID) of the neighbor
Priority – The priority of the neighbor for the router election process
State – Whether the neighbor is a DR, BDR, or DROTHER.
Dead Time - How long the router waits until it declares the neighbor down if it does not hear another hello packet within that time (The default is 40 seconds on a LAN).
Address - The neighbor’s interface IP address from which the hello packet was sent
Interface - The local router interface used to reach that neighbor

## Slide 6: Troubleshooting OSPFv2 Troubleshooting OSPFv2 Neighbor Relationships
The following are some of the reasons an OSPFv2 neighbor relationship might not form:
Interface is down - The interface must be up/up.
Interface not running the OSPF process - If the interface is not enabled for OSPF, it does not send hello packets or form adjacencies.
Mismatched timers - Hello and dead timers must match between neighbors.
Mismatched area numbers - The two ends of a link must be in the same OSPF area.
Mismatched area type - In addition to a normal OSPF area type, an area type could be a stub area or a not-so-stubby area (NSSA). The routers must agree on the type of area they are in.
Different subnets - Neighbors must be in the same subnet.

## Slide 7: Troubleshooting OSPFv2 Troubleshooting OSPFv2 Neighbor Relationships (Cont.)
Passive interface - The passive interface feature suppresses the sending and receiving of hello packets while still allowing the interface’s network to be advertised.
Mismatched authentication information - Both OSPF interfaces must be configured for matching authentication
ACLs - An ACL may be denying packets to the OSPF multicast address 224.0.0.5.
MTU mismatch - The maximum transmission unit of neighboring interfaces must match.
Duplicate router IDs - Router IDs must be unique.
Mismatched network types - neighbors configured with a different OSPF network type might not form an adjacency.

## Slide 8: Troubleshooting OSPFv2 Adjacency States
Adjacencies are not established upon the immediate receipt of hello messages. Rather, an adjacency transitions through the various states.
See Table 8-2 for adjacency states.

## Slide 9: Troubleshooting OSPFv2 OSPF Basic Configuration Errors
When an OSPF neighbor relationship does not form you need the assistance of an accurate physical and logical network diagram and the show cdp neighbors command to verify who should be the neighbors.
When troubleshooting OSPF adjacencies, you need to verify router OSPF configurations and status with various show commands like show ip interface brief and show ip protocols
Router interfaces must be up/up if you plan on forming an OSPF neighbor adjacency.
OSPF passive-interface interface command targeting the wrong interface will prevent hello packets from being sent and neighbor adjacency from forming.
Router OSPF network ip_address wildcard_mask area area_id command or ip ospf process_id area area_id interface command configured on the wrong interfaces or in the wrong area IDs can also prevent neighbor relationships from forming.
If an interface is enabled for OSPF with both the network ip_address wildcard_mask area area_id command and the ip ospf process_id area area_id command, the ip ospf process_id area area_id command takes precedence.

## Slide 10: Troubleshooting OSPFv2 Mismatched Timers
OSPF timers must match for neighbor adjacencies to form (with EIGRP they do not). The hello timer defaults to 10 seconds for broadcast and point-to-point network types and 30 seconds for nonbroadcast and point-to-multipoint network types. The dead timer defaults to 40 seconds for broadcast and point-to-point network types and 120 seconds for nonbroadcast and point-to-multipoint network types.
Verify current timers on an OSPF interface, with the show ip ospf interface interface_type interface_number command
You can use the debug ip ospf hello command when troubleshooting adjacencies to reveal mismatched timers, as shown in Example 8-5. In this example, the packet received (R) has a dead timer of 44 and a hello timer of 11. The local device (C) has a dead timer of 40 and a hello timer of 10.

## Slide 11: Troubleshooting OSPFv2 Mismatched Area Numbers
For OSPF routers to form neighbor adjacencies, their neighboring interfaces must be in the same area. You can verify the area an OSPF interface by using either one of the following show commands:
R1# show ip ospf interface interface_type interface_number
R1# show ip ospf interface brief
You can use a debug command when troubleshooting adjacencies to find mismatched area numbers:
R1# debug ip ospf adj
In Example 8-8. In this example, the packet received has an area ID of 1, and the local interface is participating in Area 2.

## Slide 12: Troubleshooting OSPFv2 Mismatched Area Type
For routers within an area to form adjacencies, they must agree on the area type. Within the hello packet, a stub area flag is designed to indicate the type of area the neighbor is in.
You can verify the types of areas connected to a router by using the show ip protocols command.
Example 8-9 displays the output of show ip protocols.
If there is a router with multiple areas connected to it, you can verify the areas and their type by using the show ip ospf command, as shown in Example 8-9.
In Example 8-10 , the debug ip ospf hello command is used to find mismatched area types.

## Slide 13: Troubleshooting OSPFv2 Subnets and Passive Interfaces
Different Subnets - To form an OSPF neighbor adjacency, the router interfaces must be on the same subnet.
Passive Interface - Ensures that rogue routers will not be able to form adjacencies with a legitimate router on an interface since it is not sending or receiving OSPF packets on that interface. However, if you configure the wrong interface as passive, a legitimate OSPF neighbor relationship is not formed.

## Slide 14: Troubleshooting OSPFv2 Mismatched Authentication Information
Both routers must agree on the settings for a neighbor relationship to form. To verify whether authentication has been enabled for the entire area on a router, you use the show ip ospf command.
To verify the key ID being used on an interface-by-interface basis use the show ip ospf interface interface_type interface_number command.
In addition, you must verify the case-sensitive key string that is being used by using the show running-config command.
If you configure authentication on an interface-by-interface basis you need to check the output of show ip ospf interface command.
You can use the debug ip ospf adj command to find mismatched authentication information.

## Slide 15: Troubleshooting OSPFv2 ACL and MTU Mismatch
ACL (Access List) - If an ACL is applied to an interface, and the ACL is not permitting OSPF packets, a neighbor relationship does not form. Notice that ACL 100 is applied inbound on interface GigabitEthernet1/0. Note that outbound ACLs do not affect OSPF packets. Therefore, if there is an outbound ACL configured on an interface and a neighbor adjacency is not forming, the ACL is not the problem because the outbound ACL does not apply to OSPF packets generated on the local router.
MTU Mismatch - For OSPF routers to become neighbors and achieve full adjacency, the interface of each router forming the adjacency must have the same MTU. If they don’t, the routers can see each other but get stuck in the ExStart/Exchange states. In Example 8-18, the output of show ip ospf neighbor indicates that R1 is stuck in the Exchange state, and that R2 is stuck in the ExStart state. To solve this issue, you can manually modify the MTU values of the interfaces so that they match, or you can use the ip ospf mtu-ignore interface configuration command, which stops OSPF from comparing the MTU when trying to form an adjacency.

## Slide 16: Troubleshooting OSPFv2 Duplicate Router ID
OSPF neighbor relationships do not form between routers if they have the same RID. When a duplicate RID exists, you receive a syslog message similar to the following:
%OSPF-4-DUP_RTRID_NBR: OSPF detected duplicate router-id 10.1.23.2 from 10.1.12.2 on interface GigabitEthernet1/0
If you manually change the RID with the router-id ip_address command in router OSPF configuration mode, you must reset the OSPF process by using the clear ip ospf process command in order for it to take effect.

## Slide 17: Troubleshooting OSPFv2 Mismatched Network Types
OSPF supports multiple network types. Different network types have different default values. Therefore, if two OSPF routers that are trying to form a neighbor adjacency are configured with noncompatible network types, a neighbor relationship does not form.
For example, if the network type is Broadcast on R1’s interface and NBMA on R2’s interface,
the timers do not match, and the adjacency does not form. Table 8-3 lists the OSPF network
types and their characteristics.
To determine the network type associated with an OSPF-enabled interface, you can issue the
command show ip ospf interface interface_type interface_number.

## Slide 18: Troubleshooting OSPFv2 Routes
This section examines the reasons OSPF routes might be missing and how to determine the reason a route is missing.

## Slide 19: Troubleshooting OSPFv2 Routes Common Reasons for Missing OSPFv2 Routes
OSPF routers receive LSAs from every router within the same area. Every router in an area must have exactly the same link-state database (LSDB) for that area. If you have no neighbors, you will not learn any routes.
Following is a list of common reasons OSPF routes might be missing either from the LSDB or the routing table:
Interface not running the OSPF process - If the interface is not participating in the OSPF process, the network the interface is part of is not injected into the OSPF process and is therefore not advertised to neighbors.
Better source of information - If exactly the same network is learned from a more reliable source, it is used instead of the OSPF-learned information.
Route filtering - A filter might be preventing a route from being installed in the routing table.
Stub area configuration - If the wrong type of stub area is chosen, you might be receiving a default route instead of the actual route.
Interface is shut down - The OSPF-enabled interface must be up/up for the network associated with the interface to be advertised.
Wrong designated router elected - In a hub-and-spoke environment, if the wrong router is the DR, routes are not exchanged properly.
Duplicate RIDs - If there are two or more routers with the same RID, routes are missing in the topology.

## Slide 20: Troubleshooting OSPFv2 Routes Route Filtering
A distribute list applied to an OSPF process controls which routes are installed into the routing table from the LSDB. Note that this differs from EIGRP, where the distribute list controls routes sent and received between neighbors. The reason this difference exists is that all OSPF routers in an area must have the same LSDB.
To apply a route filter to OSPF, the distribute list is applied in OSPF configuration mode inbound (meaning into the routing table), and the routes installed are controlled by ACLs, prefix lists, or route maps.
When troubleshooting route filtering for OSPF, consider the following:
Is the distribute list applied in the correct direction?
If the distribute list is using an ACL, is the ACL correct?
If the distribute list is using a prefix list, is the prefix list correct?
If the distribute list is using a route map, is the route map correct?
The show ip protocols command identifies whether a distribute list is applied to the OSPF process.

## Slide 21: Troubleshooting OSPFv2 Routes Route Filtering (Cont.)
To verify the entries in the prefix list, you issue the show ip prefix-list TEST command, as shown in Example 8-30. If an ACL is applied, you issue the show access-list command. If a route map is applied, you issue the show route-map command. As shown in Example 8-30, you can verify the command that was used to apply the distribute list in the running configuration.
Notice in Example 8-31 that the LSDB still has the 10.1.23.0/24 network listed, but it is not installed in the routing table because of the distribute list that is denying 10.1.23.0/24 from being installed.

## Slide 22: Troubleshooting OSPFv2 Routes Stub Area Configuration
Stub areas or NSSAs, suppress Type 5 External LSAs from entering an area at the ABR. Totally stubby areas and totally NSSAs, suppress Type 5 External and Type 3 Summary LSAs from entering an area at the ABR. The routes that would have been learned from the Type 5 and Type 3 LSAs are now replaced by a default route.
With only a default route, the router loses visibility of the overall network, which could produce suboptimal routing in redundant environments.
If you are expecting a Type 5 or Type 3 LSA for a specific route, but it is not showing up in the area, you should verify whether the area is a stub area or an NSSA and determine what types of routes are being suppressed. You can verify whether the area connected to the router is a stub area or an NSSA by using the show ip ospf command, as shown in Example 8-32.

## Slide 23: Troubleshooting OSPFv2 Routes Stub Area Configuration (Cont.)
With totally stubby areas or totally NSSAs you configure the no-summary keyword on the ABR. It is not needed on the other routers. Therefore, it is best to review the output of show ip ospf on the ABR.
In Example 8-33, R2 is configured to suppress Type 3 and Type 5 LSAs from entering Area 1 and replacing them with a default route. So even though R1 appears to be in a stub area, it is really in a totally stubby area, based on the configuration of R2.

## Slide 24: Troubleshooting OSPFv2 Routes Wrong DR Elected
In a subnet with multiple routers it does not matter which router is elected as the DR (multi-access Ethernet topology or a full-mesh Frame Relay topology) because every router is able to reach the DR.
It does matter who the DR is over a hub-and-spoke nonbroadcast multi-access (NBMA) network such as Frame Relay or with a Dynamic Multipoint VPN (DMVPN), because the underlying Layer 2 topology does not line up with the Layer 3 addressing.
Figure 8-3 shows a hub-and-spoke Frame Relay or DMVPN network.

## Slide 25: Troubleshooting OSPFv2 Routes Wrong DR Elected (Cont.)
Figure 8-4 shows the wrong DR placement.
The DR router needs to be reachable through a single hop because of how OSPF neighbor relationships are formed and how routers communicate with the DR. Hellos are established with the multicast address 224.0.0.5, and the DR is reachable at the multicast address 224.0.0.6. Packets destined to these two multicast addresses are not relayed by other routers.
Because the DR is responsible for relaying learned routes in a multi-access network, it needs to be centrally located. In this case, you need to control who the DR is. It must be R1 to ensure that all routers are able to send LSAs to it and receive LSAs from it, as shown in Figure 8-5.

## Slide 26: Troubleshooting OSPFv2 Routes Duplicate Router IDs
The OSPF router ID (RID) is used in forming neighbor relationships and to determine which router is advertising a specific LSA, it is imperative that the RIDs are unique in the domain.
If there are duplicate RIDs, the network issues can vary. Having duplicate RIDs in different areas would cause the physical OSPF topology to be different from the way the SPF algorithm sees it. This can cause routing issues because some routes may not be passed between areas, causing the LSDB and the routing tables to be incomplete.

## Slide 27: Troubleshooting Miscellaneous OSPFv2 Issues
This section looks at tracking LSAs through the network, route summarization, discontiguous areas, load balancing, and default routes.

## Slide 28: Troubleshooting Miscellaneous OSPFv2 Issues Tracking OSPF Advertisements Through a Network
The following steps describe how network 192.168.1.0/24, connected to R1, is learned by the LSDBs of routers R2, R3, R4, and R5:
Step 1. Router R1 creates a Type 1 LSA for the 192.168.1.0/24 network and floods it into Area 1
Step 2. Router R2 receives the router LSA for 192.168.1.0/24 and places it in the Area 1 LSDB. R2 runs the SPF algorithm to determine the best path to reach the 192.168.1.0/24 network. The best result is placed in R2’s routing table (RIB).
Step 3. Router R2 informs Area 0 routers about network 192.168.1.0/24 by injecting a Type 3 LSA about the network into the LSDB of Area 0 and flooding it into Area 0. This LSA includes the cost to reach the 192.168.1.0/24 network, from the perspective of router R2.

## Slide 29: Troubleshooting Miscellaneous OSPFv2 Issues Tracking OSPF Advertisements Through a Network (Cont.)
Step 4. Each of the other Area 0 routers, R3 and R4, receives the Type 3 LSA and adds it to its Area 0 LSDB. These routers run the SPF algorithm to determine the cost to reach R2. This cost is then added to the cost R2 advertised in its Type 3 LSA, and the result is stored in the RIBs
Step 5. Router R4 informs Area 2 routers about network 192.168.1.0/24 by injecting a Type 3 LSA about the network into the LSDB of Area 2 and flooding it into Area 2. This LSA includes the cost to reach the 192.168.1.0/24 network, from the perspective of R4.
Step 6. Each of the routers in Area 2 receives the Type 3 LSA and adds it to its Area 2 LSDB. These routers run the SPF algorithm to determine the cost to reach R4. This cost is then added to the cost router R4 advertised in its Type 3 LSA, and the result is stored in the RIB of the routers.

## Slide 30: Troubleshooting Miscellaneous OSPFv2 Issues Types of OSPFv2 LSAs
To successfully troubleshoot OSPF-related issues, you should have a solid understanding of how OSPF routers discover networks and the different types of OSPF LSAs.
Table 8-4 lists the LSA types you commonly encounter when troubleshooting a Cisco-based OSPF network.

## Slide 31: Troubleshooting Miscellaneous OSPFv2 Issues Route Summarization
With OSPF, manual route summarization is enabled on an area-by-area basis on an ABR and on an ASBR to summarize external routes being injected into an area.
When troubleshooting route summarization, you need to keep in mind the following:
Did you enable route summarization on the correct router?
Did you enable route summarization for the correct area?
Did you create the appropriate summary route?
Remember that interarea summaries are created on ABRs with the area area-id range ip-prefix command and that external summaries are created on ASBRs with the summary-address ip-prefix/length command.
When a summary route is created on a router, so is a summary route to Null0:
R2# show ip route | include Null
O 10.1.0.0/16 is a summary, 00:16:07, Null0
This route to Null0 is created and installed in the routing table to prevent routing loops. It is imperative that this route be in the table to ensure that if a packet received by this router and destined to a network that falls within the summary, but for which the router does not know how to reach (longer match), it is dropped.

## Slide 32: Troubleshooting Miscellaneous OSPFv2 Issues Discontiguous Areas and Virtual Links
In a multiarea OSPF network, the backbone area (Area 0) must exist, and all other areas must connect to Area 0. If an area is not physically adjacent to Area 0, routes are not successfully learned by all routers in the OSPF domain. To solve this issue, a virtual link can be configured to logically connect the nonadjacent area with Area 0.
A virtual link is created between the routers connected to the transit area (Area 1) by using their RIDs and the transit area number. The router OSPF configuration mode command on R2 is area 1 virtual-link 4.4.4.4, and the command on R4 is area 1 virtual-link 2.2.2.2. Common virtual link mistakes are, not configuring the area with the transit area or incorrectly configuring the router-ids

## Slide 33: Troubleshooting Miscellaneous OSPFv2 Issues Verifying Virtual Links
Example 8-40 Notice the local interface is OSPF_VL0, which refers to the virtual link interface.
Example 8-41 shows the output of show ip ospf virtual-links, which provides more details about the virtual link. It is not only important to verify that the virtual link is up but that the state is full, which indicates that LSAs have been successfully exchanged.

## Slide 34: Troubleshooting Miscellaneous OSPFv2 Issues Load Balancing
OSPF supports only equal-cost load balancing. Therefore, when troubleshooting load balancing for OSPF, your two primary points of concern are the overall end-to-end cost and the maximum number of paths permitted for load balancing. To verify the maximum number of equal-cost paths an OSPF router is currently configured to support, use the show ip protocols command, as shown in Example 8-42.
If your topology is showing multiple paths to reach certain networks in your organization but they are not all showing up in the routing table, it is than likely because they are not equal-cost paths or the maximum paths value is configured too low.

## Slide 35: OSPFv2 Trouble Tickets
This section presents three trouble tickets related to troubleshooting OSPF related issues

## Slide 36: OSPFv2 Trouble Tickets Trouble Ticket 8-1
All trouble tickets in this section are based on the topology shown in Figure 8-12.
Problem: Users in the 10.1.1.0/24 network indicate that they are not able to access resources in the 192.168.1.0/24 network.
As always, the first item on the list for troubleshooting is to verify the problem. You access a PC in the 10.1.1.0/24 network and ping an IP address in the 192.168.1.0/24 network; the ping is successful (0% loss), as shown in Example 8-43. However, notice that the reply is from the default gateway at 10.1.1.1, and it states Destination host unreachable. Therefore, the ping is actually technically not successful.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 37: OSPFv2 Trouble Tickets Trouble Ticket 8-2
Problem: Users in the 10.1.1.0/24 network indicate that they are not able to access resources in the 192.168.1.0/24 network.
As always, the first item on the list for troubleshooting is to verify the problem. You access a PC in the 10.1.1.0/24 network and ping an IP address in the 192.168.1.0/24 network, and it is successful (0% loss), as shown in Example 8-57. However, notice that the reply is from 10.1.23.2, and it states TTL expired in transit. Therefore, it was technically not successful.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 38: OSPFv2 Trouble Tickets Trouble Ticket 8-3
All trouble tickets in this section are based on the topology shown in Figure 8-12.
Problem: Routers R1 and R2 are not forming a neighbor adjacency
The first item on the list for troubleshooting is to verify the problem. You access R1 and issue the show ip ospf neighbor command, as shown in Example 8-64, and it confirms that there is no neighbor relationship with R2.
Refer to your text for next steps and examples to troubleshoot and resolve this trouble ticket.

## Slide 39: Prepare for the Exam

## Slide 40: Prepare for the Exam Key Topics for Chapter 8
Description
Verifying OSPF neighbors with show ip ospf neighbor
Reasons an OSPF neighbor relationship might not form
Adjacency states
Verifying OSPF interfaces with show ip ospf interface brief
Displaying OSPF interface timers on R1 Gigabit Ethernet 1/0
Mismatched area numbers
Determining the type of OSPF areas
The passive interface feature and troubleshooting passive interface issues
Verifying OSPF area authentication

## Slide 41: Prepare for the Exam Key Topics for Chapter 8 (Cont.)
Description
Verifying OSPF authentication key
MTU mismatch
OSPF network types and characteristics
Reasons an OSPF route might be missing from either the LSDB or the routing table
Considerations when troubleshooting router filtering
Stub area configuration
The importance of the DR election in a hub-and-spoke multi-access network
OSPFv2 LSAs
Considerations when troubleshooting route summarization issues
Verifying the virtual link

## Slide 42: Prepare for the Exam Key Terms for Chapter 8
Term | 
OSPF interface table | OSPFv3
OSPF neighbor table | address families
OSPF link-state database (LSDB) | designated router
link-state advertisement (LSA) | backup designated router
Dijkstra’s shortest path first (SPF) algorithm | stub area
OSPF area | totally stubby area
virtual link | NSSA
OSPF area border router (ABR) | totally NSSA
OSPF autonomous system boundary router (ASBR) | 

## Slide 43: Prepare for the Exam Command Reference for Chapter 8
Task | Command Syntax
Display the IPv4 routing protocols enabled on the device; for OSPFv2, display whether any route filters are applied, the RID, the number of areas the router is participating in, the types of areas, the maximum paths for load balancing, the network area command, the interfaces explicitly participating in the routing process, passive interfaces, routing information sources, and the AD show ip protocols | show ip protocols
Display general OSPF parameters, including the PID, the RID, the reference bandwidth, the areas configured on the router, the types of areas (stub, totally stubby, NSSA, and totally NSSA), and area authentication | show ip ospf
Display the interfaces that are participating in the OSPF process | show ip ospf interface brief
Display detailed information about the interfaces participating in the OSPF process, including interface IPv4 address and mask, area ID, PID, RID, network type, cost, DR/BDR, priority, and timers | show ip ospf interface

## Slide 44: Prepare for the Exam Command Reference for Chapter 8 (Cont.)
Task | Command Syntax
Display the OSPF devices that have formed a neighbor adjacency with the local router | show ip ospf neighbor
Display the OSPF routes that have been installed in the IPv4 routing table | show ip route ospf
Display the OSPF link-state database | show ip ospf database
Provide information about the status of OSPF virtual links that are required for areas not physically adjacent to the backbone area (that is, Area 0) | show ip ospf virtual-links
Display real-time information related to the exchange of OSPF hello packets; useful for identifying mismatched OSPF timers and mismatched OSPF area types | debug ip ospf hello
Display the transmission and reception of OSPF packets in real time | debug ip ospf packet

## Slide 45: Prepare for the Exam Command Reference for Chapter 8 (Cont.)
Task | Command Syntax
Display real-time updates about the formation of an OSPF adjacency; useful for identifying mismatched area IDs and authentication information | debug ip ospf adj
Display real-time information about OSPF events, including the transmission and reception of hello messages and LSAs; might be useful on a router that appears to be ignoring hello messages received from a neighboring router | debug ip ospf events