## Slide 1: Chapter 9: OSPFv3
Instructor Materials
CCNP Enterprise: Advanced Routing

## Slide 2: Chapter 9 Content
This chapter covers the following content:
OSPFv3 Fundamentals - This section provides an overview of the OSPFv3 routing protocol, its similarities to OSPFv2, and its configuration.
OSPFv3 Configuration - This section explains and demonstrates how OSPFv3 is used for exchanging IPv6 routes.
OSPFv3 LSA Flooding Scope - This section provides a deeper view of the OSPFv3 link-state advertisement (LSA) structure and the comparison to OSPFv2.

## Slide 3: OSPFv3 Fundamentals
Open Shortest Path First version 3 (OSPFv3) is the latest version of the OSPF protocol.
The OSPFv3 protocol is not backward compatible with OSPFv2, but the protocol mechanisms are essentially the same.

## Slide 4: OSPFv3 Fundamentals OSPFv2 and OSPFv3 Differences
The primary differences between OSPFv2 and OSPFv3 protocols are as follows:
Support for multiple address families - OSPFv3 supports IPv4 and IPv6 address families.
New LSA types - New LSA types have been created to carry IPv6 prefixes.
Removal of addressing semantics - The IP prefix information is no longer present in the OSPF packet headers.
LSA flooding - OSPFv3 includes a new link-state type field that is used to determine the flooding scope of LSA, as well as the handling of unknown LSA types.
Packet format - OSPFv3 runs directly over IPv6, and the number of fields in the packet header has been reduced.
Router ID - The router ID is used to identify neighbors, regardless of the network type in OSPFv3.
Authentication - Neighbor authentication has been removed from the OSPF protocol and is now performed through IPsec extension headers in the IPv6 packet.
Neighbor adjacencies - OSPFv3 inter-router communication is handled by IPv6 link-local addressing.
Multiple instances - OSPFv3 packets include an instance ID field that may be used to manipulate which routers on a network segment are allowed to form adjacencies.

## Slide 5: OSPFv3 Fundamentals OSPFv3 Link-State Advertisement
The OSPF link-state database (LSDB) information is organized and advertised differently in version 3 than in version 2. OSPFv3 modifies the structure of the router LSA (Type 1), renames the network summary LSA to the inter-area prefix LSA, and renames the autonomous system boundary router (ASBR) summary LSA to inter-area router LSA.
IP address information is advertised independently by two new LSA types:
  Intra-area prefix LSA
  Link-local LSA
Advertising the IP address information using new LSA types eliminates the need for OSPF to perform full shortest path first (SPF) tree calculations every time a new address prefix is added or changed on an interface. The OSPFv3 LSDB creates a shortest path topology tree based on links instead of networks.

## Slide 6: OSPFv3 Fundamentals OSPFv3 LSA Types
Table 9-2 provides a brief description of each OSPFv3 LSA type.

## Slide 7: OSPFv3 Fundamentals OSPFv3 Communication
OSPFv3 packets use protocol ID 89, and routers communicate with each other using the local interface’s IPv6 link-local address as the source. Depending on the packet type, the destination address is either a unicast link-local address or the multicast link-local scoped address:
FF02::05: OSPFv3 AllSPFRouters
FF02::06: OSPFv3 AllDRouters designated router (DR) router

## Slide 8: OSPFv3 Configuration
The following section explains the process for configuring and verifying OSPFv3.

## Slide 9: OSPFv3 Configuration OSPFv3 Configuration
The process for configuring OSPFv3 involves the following steps:
Step 1. Initialize the routing process by enabling ipv6 unicast-routing on the router and then configuring OSPFv3 with the command router ospfv3 [process-id].
Step 2. Define the router ID (RID) by using the command router-id. The router ID is a 32-bit value that does not need to match an IPv4 address. It may be any number, as long as the value is unique within the OSPF domain. OSPFv3 uses the same algorithm as OSPFv2 for dynamically locating the RID. If there are not any IPv4 interfaces available, the RID is set to 0.0.0.0 and does not allow adjacencies to form.
Step 3. Initialize the address family within the routing process by using the optional command address-family {ipv6 | ipv4} unicast. The appropriate address family is enabled automatically when OSPFv3 is enabled on an interface.
Step 4. Use the interface command ospfv3 process-id ipv6 area area-id to enable the protocol and assign the interface to an area.

## Slide 10: OSPFv3 Configuration OSPFv3 Topology
Figure 9-1 shows a simple four-router topology to demonstrate OSPFv3 configuration. Area 0 consists of R1, R2, and R3, and Area 34 contains R3 and R4. R3 is the area border router (ABR).
Example 9-1 provides the OSPFv3 and IPv6 address configurations for R1.

## Slide 11: OSPFv3 Configuration OSPFv3 Verification
The commands for viewing OSPFv3 settings and statuses are very similar to those used in
OSPFv2. In essence, you replace ip ospf with ospfv3. For example, to view neighbor adjacencies use the command show ip ospfv3 neighbor. To view an OSPFv3-enabled interface status use the command show ospfv3 interface [interface-id]

## Slide 12: OSPFv3 Configuration OSPFv3 Verification (Cont.)
The command show ospfv3 interface brief shows a brief version of the OSPFv3 interface settings. To view the OSPFv3 IPv6 routing table use the command show ipv6 route ospf.

## Slide 13: OSPFv3 Configuration Passive Interface
An interface is marked as being passive with the command passive-interface interface-id or globally with the passive-interface default; an interface is marked as active with the command no passive-interface interface-id.
The command is placed under the OSPFv3 process or under the specific address family.
Placing the command under the global process cascades the setting to both address families.
Example 9-6 demonstrates making the LAN interface on R1 explicitly passive and making all interfaces passive on R4 while marking the Gi0/3 interface as active.
The active/passive state of an interface is verified by examining the OSPFv3 interface status
using the command show ospfv3 interface [interface-id] and searching for the passive keyword.

## Slide 14: OSPFv3 Configuration IPv6 Route Summarization
Summarization of internal OSPFv3 routes follows the same rules as for OSPFv2 and must occur on ABRs by using the command area area-id range prefix/prefix-length.
Example 9-8 shows R3’s configuration for summarizing these prefixes.
Example 9-9 shows R4’s IPv6 routing table after R3 is configured to summarize the Area 0 loopback interfaces. The summary route is highlighted.

## Slide 15: OSPFv3 Configuration Network Type
OSPFv3 supports the same OSPF network types as OSPFv2. Example 9-10 shows how to view the OSPFv3 network type.
Example 9-11 demonstrates changing the OSPFv3 network type by using the interface parameter command ospfv3 network {point-to-point | point-to-multipoint broadcast | nonbroadcast}.
Example 9-12 shows how to verify the new settings. The network is now a point-to-point
link, and the interface state is indicated as P2P as confirmation.

## Slide 16: OSPFv3 Configuration OSPFv3 Authentication
OSPFv3 does not support neighbor authentication within the protocol itself. Instead, the routing protocol utilizes IP Security (IPsec) to provide authentication. IPv6 Authentication Header (AH) or Encapsulating Security Payload (ESP) extension headers may be added to the OSPF packets to provide authentication, integrity, and confidentiality:
Authentication Header (AH): Provides authentication
Encapsulating Security Payload (ESP): Provides authentication and encryption

## Slide 17: OSPFv3 Configuration OSPFv3 Authentication (Cont.)
OSPFv3 authentication supports IPsec AH authentication using the command ospfv3
authentication or ESP authentication and encryption with the command ospfv3 encryption.
OSPFv3 neighbor authentication does not perform Internet Key Exchange (IKE) to negotiate the IPSec security association (SA) values. Therefore, the IPsec Security Parameter Index (SPI) hash algorithm and key must be manually defined when configuring OSPFv3 authentication.
IPsec peers cannot reuse the same SPI values.
The command show crypto ipsec sa | include spi may be used to determine the active IPsec sessions and currently used SPI values. The full interface command ospfv3 encryption {ipsec spi spi esp encryption-algorithm {key-encryption-type key} authentication-algorithm {key-encryption-type key} | null} encrypts and authenticates the OSPFv3 packet in IOS using ESP.

## Slide 18: OSPFv3 Configuration OSPFv3 Interface Authentication and Encryption
Example 9-13 demonstrates how to configure encryption and authentication for OSPFv3 packets using ESP. The following fabricated values are included in the configuration to establish the IPsec session:
Security policy index: = 500
Encryption algorithm: = 3des
Encryption key: = 012345678901234567890123456789012345678901234567
Authentication algorithm: = sha1
Authentication key: = 0123456789012345678901234567890123456789

## Slide 19: OSPFv3 Configuration OSPFv3 Area Authentication and Encryption (Cont.)
Example 9-14 demonstrates how to configure area authentication and encryption using the same IPsec settings.
Example 9-15 displays the output of the command show ospfv3 interface [interface id]. This show command can be used to verify that authentication and encryption are enabled on the interface and that a secure connection has formed with the neighbor.

## Slide 20: OSPFv3 Configuration OSPFv3 Link-Local Forwarding
Significant changes have occurred in how OSPFv3 builds the area topology. The OSPFv3 LSDB creates a shortest path topology tree based on links instead of networks. This means that transit links only require IPv6 link-local addresses for forwarding traffic.
Example 9-16 demonstrates the removal of the global IPv6 unicast addresses from the transit links on R1, R2, and R3.

## Slide 21: OSPFv3 Configuration OSPFv3 Link-Local Forwarding (Cont.)
Example 9-17 shows the OSPFv3 learned routes from R4’s perspective. Notice that the transit networks no longer appear.
R4 still maintains full connectivity to those networks in Example 9-17 because the topology is built using the IPv6 link-local address. As long as the source and destination devices have routes to each other, communication can still exist.
Example 9-18 demonstrates that R4 still maintains connectivity to R1’s LAN interface.

## Slide 22: OSPFv3 LSA Flooding Scope
OSPFv3 allows for three flooding scopes: link-local scope, area scope and autonomous system scope.

## Slide 23: OSPFv3 LSA Flooding Scope OSPFv3 LSA Flooding Scope
The OSPFv3 flooding scopes:
Link-local scope - Limited to the local link
Area scope - Contains LSA flooding to the local area
Autonomous system scope - Floods LSAs throughout the entire OSPF routing domain
The LS type field in OSPFv3 has been modified from 8 bits to 16 bits.
Figure 9-3 shows the new LS Type field format.
The 3 high-order bits of the new LS Type field allow for the encoding of flood information.
The first bit, U (unrecognized), indicates how a router should handle an LSA if it is unrecognized.
The second and third bits, both S (scope) bits, indicate how the LSA should be flooded.
The remaining bits of the link-state field indicate the function code of the LSA.

## Slide 24: OSPFv3 LSA Flooding Scope OSPFv3 Database
The router LSA describes the router’s interface state and cost.
Example 9-19 shows the output of the command show ospfv3 database router[self-originate | adv-router RID].
The optional self-originate keyword filters the LSAs to those created by the router on which the command is executed. The adv-router RID keyword allows for selection of the LSAs for a specific router’s LSAs that exist in the local router’s LSDB.

## Slide 25: OSPFv3 LSA Flooding Scope OSPFv3 Options
OSPFv3 LSAs include an options bit field that describes the router’s capabilities. Table 9-5 describes the various service options.
Example 9-20 shows a portion of R3’s router LSA’s LSDB. The highlighted bits indicate the functionality the router can perform in each area.

## Slide 26: OSPFv3 LSA Flooding Scope OSPFv3 Database Network
Example 9-21 shows the output of the command show ospfv3 database network [self-originate].
The link LSA is responsible for providing details for the IPv6 prefixes associated with an interface. Example 9-22 shows the output of the command show ospfv3 database link [self-originate].

## Slide 27: OSPFv3 LSA Flooding Scope OSPFv3 LSDB
Example 9-23 shows R3’s database. Notice that R3’s router LSA bits are set to B, indicating that it is an ABR router.

## Slide 28: Prepare for the Exam

## Slide 29: Prepare for the Exam Key Topics for Chapter 9
Description
OSPFv3 fundamentals
OSPFv3 link-state advertisement
OSPFv3 communication
OSPFv3 configuration
OSPFv3 verification
IPv6 route summarization
Network type
OSPFv3 authentication
OSPFv3 flooding scope

## Slide 30: Prepare for the Exam Command Reference for Chapter 9
Task | Command Syntax
Configure OSPFv3 on a router and enable it on an interface | router ospfv3 [process-id] interface interface-id ospfv3 process-id {ipv4 ¦ ipv6} area area-id
Configure a specific OSPFv3 interface as passive | passive-interface interface-id
Configure all OSPFv3 interfaces as passive | passive-interface default
Summarize an IPv6 network range on an ABR | area area-id range prefix/prefix-length
Configure an OSPFv3 interface as point-to-point or broadcast network type | ospfv3 network {point-to-point ¦ broadcast}
Display OSPFv3 interface settings | show ospfv3 interface [interface-id]
Display OSPFv3 IPv6 neighbors | show ospfv3 ipv6 neighbor
Display OSPFv3 router LSAs | show ospfv3 database router
Display OSPFv3 network LSAs | show ospfv3 database network
Display OSPFv3 link LSAs | show ospfv3 database link