## Slide 1
DIO Module
Module front, removed
Module label, removed
To remove the front:
Remove the label with a thin knife edge
For latches, start with 1 latch and work your way around with a flat bladed screwdriver, gently prying each latch a little. After a few rounds, the front will begin to separate (*)
* I broke 1 of 8 latches, so not bad

## Slide 2
To remove the top cover, slide the top unit in the direction of the arrow – towards the back of the module about 3/16 to clear unseen latch
Slide this way
Module Front
Module Back
Top View of Module

## Slide 3
U6
U5
U4
U3
U2
U1
X2
X3
X1
Pin 1
Pin 36
Card edge connector to base unit
Slot connector for I/O ports
36 Pins

## Slide 4
U6
U5
U4
U3
U2
U1
X2
X3
X1
Pin 1
Pin 36
Card edge connector to base unit
Slot connector for I/O ports
36 Pins
X1 – CSB 250D
X2 – AZ830-2C-5DSE
X3 – AZ830-2C-5DSE
U1 – A1020A-PL68C
U2 – SN75C189N
U3 – SN75C189N
U4 – SN754410NE
U5 – SN754410NE
U6 – ULN2003A
Resistors/capacitors not shown

## Slide 5
Bottom plate
These 4 clips hold the black/gray stand on the bottom of the module – pinch and it comes off

## Slide 6
Nothing on back side