## Slide 1: LTE Post launch optimization

## Slide 2: Basic Checks
Check for alarms on the site.
Check VSWR for the site.
Check to see that the cell isn’t reserved or barred.
Check if there is any drop or increase in traffic which can impact KPI’s – {Special events etc}. Check counters pmPdcpVolDlDrb, pmPdcpVolDlSrb.
Check if there is any interference. Use counter pmRadioRecInterferencePwr
Check if it is a coverage issue. Use counters pmRadioTbsPwrRestricted, pmRadioUeRepCqiDistr

## Slide 3: Main kpi’s
Accessibility
Retainability
Mobility
Throughput

## Slide 4: Accessibility
Accessibility
Overall accessibility consists of 3 portions –
a) RRC portion
b) S1 portion
c) ERAB portion
Calculating accessibility:
100*(pmRrcConnEstabSucc/(pmRrcConnEstabAtt-pmRrcConnEstabAttReAtt) * (pmS1SigConnEstabSucc/pmS1SigConnEstabAtt) * (pmErabEstabSuccInit + pmErabEstabSuccAdded) /(pmErabEstabAttInit + pmErabEstabAttAdded)

## Slide 5: RRC CONNECTION SETUP

## Slide 6: E-RAB Establishment with Initial Context Setup Procedure

## Slide 7: Accessibility issues in RRC phase
Accessibility in RRC phase points towards poor RF conditions, bad RRU or an UE trying to access the network in poor conditions. You will need to try and improve the RF conditions to see better RRC Success Rate. If it’s a bad RRU replace the RRU.
UE’s trying to access the network in poor RF conditions can be determined by looking for high pegs in pmRrcConnEstabAttReatt

## Slide 8: Accessibility issues in ERAB Phase
Accessibility in ERAB phase can happen due to an UE issue or due to hanging resources in the eNb or an RRU issue.
With regards to hanging resources in eNb – a restart normally helps. With regards to faulty RRU’s – if restarting the RRU doesn’t help, replacing the RRU is the option.
NEO is a very powerful tool to identify UE related issues. You will need cell traces and EBM traces to narrow down the UE.
Cell Traces are Active in the OSS for cells you want to investigate.
  /var/opt/ericsson/nms_umts_pms_seg/segment1/CELLTRACE
MME Traces are Active and readily available
  /var/opt/ericsson/sgw/outputfiles/sgeh/sgsn-mme

## Slide 9: Retainability
Causes for poor Retainability will normally be due to poor RF. Improve RF in the region, Maintain balance between the IRAT rate and Retainability. Reduce Interference in the region if any, Cell Range changes in cases where the cell range doesn’t match the RF footprint can also help in Retainability improvement.
Formula:(100 * (pmErabRelAbnormalEnbAct + pmErabRelMmeAct)/(pmErabEstabSuccInit+pmErabEstabSuccAdded))

## Slide 10: LTE Retainability Optimization
E-RAB Release Procedure – MME Initiated

## Slide 11: LTE Retainability Optimization:
E-RAB Release Procedure – eNB Initiated

## Slide 12: LTE Retainability Optimization
UE Context Release Procedure – MME Initiated

## Slide 13: mobility
Mobility consists of 2 portions:-Preparation phase and Execution phase.
Issues in Preparation Phase normally point towards configuration issues. Check if isHoAllowed is set to true, feature and license for intraLTE HO is enabled, No missing or disabled termpointtoMME links and handover to target is possible {target not locked}.
Issues in Execution Phase normally point towards RF issues. Check if overshooter , if it’s an ANR PCI clash, if PCI retune is required or if HO needs to be done faster or slower from source to target.
Moblility:100 * ( pmHoPrepSuccLteIntraF / pmHoPrepAttLteIntraF) * (pmHoExeSuccLteIntraF / pmHoExeAttLteIntraF)

## Slide 14: Mobility: Call Flow

## Slide 15: HO Execution failures: ANR-PCI Collision
Target eNB has same PCIs as another eNB much closer to the source. If there isn’t another eNb closer to the source, then this could indicate that the target eNb is an overshooter. You will then have to downtilt the target.
Handovers intended for closer eNB were prepared and executed to eNBs miles away
To resolve ANR-PCI clashes. Delete externalenodebfunction, externaleutrancellfdd, termpttoenb and eutrancellrelation
ANR added cells from the closer eNB as neighbors in every case, resulting in a substantial increase in Handover Success Rate

## Slide 16: Throughput
One of the first things to confirm would be parameter settings, system configuration and the RF environment.
Use of the other accessibility / retainability /mobility related KPI’s will be very helpful.
Site hardware audit (including jumpers, cables, connectors, antennas etc) would be necessary
Investigation of RF environment will have to be performed. (SINR/ antenna types and planning)
Dl THROUGHPUT= (pmPdcpVolDlDrb - pmPdcpVolDlDrbLastTTI) / (pmUeThpTimeDl)
Ul THROUGHPUT= (pmUeThpVolUL) / (pmUeThpTimeDl)

## Slide 17: Throughput Optimization

## Slide 18: Analysis Flow for Dl throughput investigation

## Slide 19: Analysis Flow for UL throughput investigation

## Slide 20: Downlink Throughput Troubleshooting
The general troubleshooting strategy is described below and the covered reasons for bad throughput are shown in the figure below

## Slide 21: Downlink Throughput Troubleshooting (contd..)
At the end of this methodology, you will be able to determine if the reasons for low throughput in your cells is one of the following or a combination, thereof.
BLER (bad coverage)
Downlink Interference (Bad CQI)
MIMO Parameters
Scheduling algorithm
Low Demand
CQI reporting frequency
Other (VSWR, Backhaul capacity)

## Slide 22: UPlink Throughput Troubleshooting
The general troubleshooting strategy is described below and the covered reasons for bad throughput are shown in the figure below.

## Slide 23: UPlink Throughput Troubleshooting (contd..)
At the end of this methodology, you will be able to determine if the reasons for low throughput in your cells is one of the following or a combination, thereof:
BLER (bad coverage)
Uplink Interference (high RSSI)
Low Power headroom
Scheduling algorithm
Low Demand
Other (VSWR, Backhaul capacity)