## Slide 1: DCIM System Planning Overview

## Slide 2
With the development of information technologies, data center facility has become increasingly important. The reliability of the facility determines service continuity. The management of key facilities in data centers has gradually evolved from traditional monitoring to unified management and intelligent operation and maintenance (O&M), that is, Data Center Infrastructure Management (DCIM). Designing the DCIM system properly will be the core work of data center O&M teams.
The slides describe the DCIM concept, differences between DCIM and traditional power and environment monitoring systems, and DCIM development trend, and introduce knowledge related to the DCIM system planning.

## Slide 3
On completion of this course, you will be able to:
  Describe the DCIM concept.
  Distinguish the DCIM and traditional power and environment monitoring systems.
  Understand the DCIM development trend.
  Describe the DCIM planning considerations and process.

## Slide 4
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process

## Slide 5: What is DCIM?
Data center infrastructure management (DCIM) is a unified management platform for data center infrastructure and IT equipment. It can maximize data center operation efficiency and improve data center availability through data analysis and aggregation.
Homepage
Notes: DCIM is a hot topic in the data center operation and management field in recent years. It originated from countries outside China. Different organizations have different definitions of DCIM. However, it is widely recognized that the DCIM system or tool can build a bridge between data center infrastructure and IT equipment to help operators manage data centers and improve operation efficiency.
  Gartner defines DCIM as follows: DCIM tools monitor, measure, manage, and/or control data center utilization and energy consumption of all IT-related equipment (such as servers, storage and network switches) and facility infrastructure components (such as power distribution units and computer room air conditioners [CRACs]).
  Wikipedia defines DCIM as follows: DCIM is the integration of information technology (IT) and facility management disciplines to centralize monitoring, management and intelligent capacity planning of a data center's critical systems. Achieved through the implementation of specialized software, hardware and sensors, DCIM enables common, real-time monitoring and management platform for all interdependent systems across IT and facility infrastructures.
Gartner: Gartner Group is the first company to conduct information technology research and analysis, providing specialized services for technology users in need.

## Slide 6: Why DCIM Appears?
Problems in data center infrastructure O&M
  Industrial technologies develop,
  advanced management concepts are
  introduced, and services are converged.
  Existing data center infrastructure has
  many problems.
  IT service equipment and infrastructure
  management are separated.
Outdated data center management modes
Why DCIM appears?
  O&M depends on human resources and
  its quality is difficult to be ensured.
  It is difficult to coordinate and analyze
  subsystem data as their display modes
  are different.
  As the business process is unclear, errors
  are prone to occur when changes occur.
Notes: Problems in O&M of traditional data center infrastructure
  With the development of industrial technologies, introduction of advanced management concepts, and service convergence, the traditional power and environment monitoring mode that focuses on infrastructure management cannot meet O&M requirements of enterprises and organizations for data centers.
  According to an Internet Data Corporation (IDC) report, 84% of data centers in the market face problems in cooling, power supply, space, and load bearing. These problems include prolonged application rollout time, increased operational expenditure (OPEX), and service interruption.
  In a traditional data center, IT equipment and infrastructure are managed by different departments. Manual organization structure division facilitates personnel management and division of rights and responsibilities to some extent, but it increases communication costs between departments, reduces the O&M efficiency of a data center, and increases the risk of data center accidents to some extent.
IDC: International Data Corporation, a world-renowned market consultation and event service provider in IT, telecommunications, and consumer technology. Its market tracking data in IT has become an industry standard.

## Slide 7: DCIM Benefits
The formula for calculating data center costs: TCO = CAPEX + OPEX.
Costs
Reduces capital expenditure (CAPEX).
  Improves resource utilization and
  increases return on investment (ROI).
  Implements visualized management of
  resources and monitors space, power,
  and cooling (SPC) in real time to avoid
  repeated and excessive investment.
Reduces operational expenditure (OPEX).
  Displays key energy consumption indicators
  in real time and analyzes and optimizes
  them initiatively.
  Monitors power consumption of data center
  servers in real time to detect low-load and
  no-load servers, providing basis for
  and optimization.
DCIM benefits
Notes: CAPEX = Strategic investment + Rolling investment.
OPEX = Maintenance costs + Marketing costs + Labor costs (+ Depreciation).
Reduces CAPEX:
  Improved resource utilization and increased revenues: For data centers, each U space is a valuable resource. The ROI can be increased by improving equipment utilization and prolonging the service life of a data center.
  Visualized modeling and quantitative monitoring of SPC: DCIM can perform visualized modeling for a data center and monitor its capacities, such as power, cooling, and space. In the design of a data center, redundancy is considered to improve reliability. In addition, the power consumption of a server cannot reach its nameplate specifications. Therefore, the actual capacity of each rack cannot be fully used. DCIM provides real-time and refined management, which enables users to learn about the resource usage of each rack and the entire data center in real time, thereby improving asset utilization, prolonging the service life of the data center, and saving investment.
CAPEX: Capital Expenditure.
OPEX: Operating Expense.
PUE: Power Usage Effectiveness.
WUE: Water Usage Effectiveness.
CUE: Carbon Usage Effectiveness.

## Slide 8
Notes: Reduces OPEX:
  Data centers are energy-hungry. Electricity costs account for a large proportion of O&M costs. Therefore, the DCIM system must monitor key energy consumption indicators such as the power usage effectiveness (PUE) of a data center and display energy consumption of IT equipment and infrastructure equipment in real time. In the future, it should also be able to monitor the water usage effectiveness (WUE) and carbon usage effectiveness (CUE).
  The DCIM system can collect information such as server power consumption and CPU usage to identify low-load and no-load servers in a data center. These servers are consolidated or removed from racks to improve equipment utilization and reduce power consumption of the data center. In addition, by combining life cycles of IT equipment and energy consumption information of servers, the DCIM system can eliminate some old servers with weak computing capabilities but high energy consumption to further save energy and improve efficiency.

## Slide 9: DCIM Software Components
During the design of DCIM software, the following components need to be considered: basic framework, application framework and web integration framework, maintenance tool framework, platform interfaces, and running environment (operating system and database).
Installation and deployment
Backup and restoration
System monitoring
Component management
…
Maintenance tool framework
Communications bus
Distributed partition management
Persistence layer service
Web user interface (UI) components
…
Basic framework
Common applications
Operations management
O&M management
Energy efficiency management
…
Application framework and web integration framework
Open API
Northbound service
…
Platform interface
DCIM
Notes: Basic framework:
  Communication bus: refers to communication trunk lines that transmit information among functional components of the DCIM software.
  Distributed partition management: The system framework provides multiple processing threads and service partitions.
  Persistence layer service: allows users to query, insert, update, and delete data.
  Web UI component: a component of the web user interface (UI).
Application framework and web integration framework:
  Common applications: involve fault management, topology management, equipment access management, security management, and performance management.
  Operation management: includes asset management and capacity management.
  Energy efficiency management: manages the energy efficiency of managed objects or regions.

## Slide 10
Notes: Maintenance tool framework:
  Installation and deployment: Maintenance tools should be able to install and deploy the DCIM software.
  Backup and restoration: Maintenance tools should be able to perform system backup and restoration.
  System monitoring: The DCIM software can be monitored and managed by maintenance tools.
  Component management: DCIM software functions and services can be added or deleted through maintenance tools.
Platform interfaces:
  Open API: An API is an application programming interface. In the Internet era, services of websites or software are encapsulated into a series of data interfaces that can be easily identified by computers and opened to third-party developers. This behavior is called open API. The platform that provides open APIs is called an open platform.
  Northbound service: Interconnects with northbound third-party management systems.

## Slide 11: DCIM Hardware Components
DCIM hardware consists of intelligent interfaces, sensors, collection devices, servers (processing and storage), network transmission devices, and display devices.
Collection device
Server
Network transmission devices
Intelligent interfaces and sensors
Display devices

## Slide 12
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process

## Slide 13: Relationship Between DCIM and Power and Environment Monitoring
A data center consists of a power supply and distribution system, cooling system, fire extinguishing system, power and environment monitoring system, integrated cabling system, lightning protection and grounding system, cabinet system, and decoration system.
A power and environment monitoring system monitors and controls power and environment equipment. A DCIM system implements unified management and dynamic optimization of all infrastructure in a data center. The DCIM system is an upgraded version of the power and environment monitoring system.
System Functions | Traditional Power and Environment Monitoring System | DCIM System
Real-time signals | √ | √
Alarm management | √ | √
Access control management | √ | √
Battery monitoring | √ | √
System management | √ | √
Video management | √ | √
Report management | √ | √
Capacity management | × | √
Asset management | × | √
Personnel management | × | √
Energy efficiency management | × | √
Process management | × | √
Cooling optimization | × | √
Tenant management | × | √
Notes: From the perspective of operation management, the main differences between the DCIM system and the power and environment monitoring system lie in data association, analysis, and optimization capabilities. The power and environment monitoring system focuses on real-time signals and alarms of key infrastructure, such as the method to converge and manage alarms timely after a fault occurs. The DCIM system focuses more on the integrity of O&M business. In addition to basic functions, the DCIM system supports comprehensive analysis of data center infrastructure based on collected data and provides service assistance and support from multiple dimensions, such as planning, optimization, prediction, and change.

## Slide 14: Relationship Between DCIM, BMS, and ITSM
Relationship between DCIM and BMS:
  In the early stage, a building management system (BMS) was used to implement power and environment monitoring for data center. In addition, subsystems such as access control management, video surveillance, and lighting control were integrated.
  The DCIM and BMS have same functions in critical infrastructure monitoring. However, in addition to that, the DCIM focuses more on monitoring, analysis, and comprehensive view display of key equipment such as cooling and power supply and distribution equipment.
Relationship between DCIM and ITSM:
  With changes of data center O&M requirements, the traditional power and environment monitoring system gradually evolves to the DCIM system. IT monitoring management gradually evolves from traditional network monitoring to IT service management (ITSM).
  ITSM focuses on logical infrastructure (such as operating systems, applications, and networks) management, while DCIM focuses on physical infrastructure management.
Notes: BMS: Building Management System.
ITSM: IT Service Management.
The DCIM system provides data center floor plan and asset capacity managements that are not involved in traditional BMS and ITSM, integrates multiple separated subsystems in a data center, and provides a unified management platform.

## Slide 15
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process

## Slide 16: DCIM Development Trend - Cloud Convergence
As the data center construction scale increases, O&M management becomes more complex and professional requirements for it become higher. Cloud services can be used to provide cloud-based capabilities of the DCIM system for more efficient, quick, and professional O&M management of data centers and sharing of O&M resources.
  Implementation mode: A cloud service agent is embedded in the DCIM server. Based on cloud technologies, the DCIM cloud service platform provides remote maintenance and management services for DCIM.
  Maintenance tools: The virtualization technology is used to release IT tools required by maintenance projects on the cloud for engineers to use anytime and anywhere, simplifying O&M.
Cloud service platform
Maintenance tools
Access portal
Mobile terminals
Web terminals
O&M teams
DCIM server
Data center
Agent services
Notes: Cloud services: They are adding, usage, and interaction models of Internet-based services. Cloud services are used to provide dynamically scalable and virtualized resources over the Internet. The term "cloud" is a metaphor for networks and the Internet. In the past, it was used to represent telecommunication networks. Later, it was also used to represent the Internet and an abstraction of underlying infrastructure. Cloud services refer to on-demand and scalable services obtained through networks. The services can be related to IT, software, and the Internet, and can also be other services.
A cloud service agent is embedded in the DCIM server. Based on cloud technologies, the DCIM cloud service platform provides remote maintenance and management for DCIM. In this way, functions of the DCIM server can be released as cloud services. Authorized maintenance personnel can log in to the DCIM cloud service platform anytime and anywhere. From the perspective of maintenance personnel, it is as convenient as operating or viewing local equipment, and has high security and traceability. The cloud service agent builds management and data transmission channels between the data center target equipment and the DCIM cloud service platform. Users can configure the list of equipment that needs to be managed and controlled in the cloud service agent.

## Slide 17: DCIM Development Trend - Intelligent O&M
Data center infrastructure O&M has gradually shifted from manual experience to process-based and standardized O&M, and will be intelligent in the future, improving O&M quality and efficiency greatly.
A large number of O&M personnel are required.
Experience and knowledge cannot be transferred in a standardized manner.
The O&M quality completely depends on personal experience and stability.
An automation system is responsible for repetitive O&M works.
Analytical works are completed with the aid of new technologies, such as cloud computing.
Reduces human resource investment greatly.
Promotes the transformation of O&M personnel.
Solidifies experience and knowledge based on standards and processes.
Develops a mechanism and system tools to drive manual work.
Performs quantitative analysis of human resource allocation.
Manual experience
Streamlined process and standardization
Intelligentization

## Slide 18: Intelligent O&M - Electronic Inspection
Electronic equipment room inspection and auxiliary mobile apps greatly reduce routine O&M labor hours.
Inspection route planning
Allows users to customize inspection routes, bind inspection equipment or areas, and edit the inspection sequence.
Generates and dispatches scheduled and automatic inspection tasks to related owners.
Allows inspection owners to use mobile apps to automatically receive inspection tasks.
Mobile room inspection
Allows users to submit inspection results in one-click mode.
Performs proactive notification of inspection tasks and content integrity self-check to ensure that the room inspection is completed timely with high quality.
Meter reading can be automatically and remotely completed, eliminating the need for manual meter reading and greatly reducing labor hours for manual inspection.
One-click inspection report
Automatically generates an inspection report to evaluate the room health.
Traces and collects statistics on room inspection progress in real time, and displays expired tasks timely.

## Slide 19: Intelligent O&M - Unattended Inspection
Inspection items of a traditional data center include collection of signals, sound, images, odor, and others (such as appearance). DCIM uses new technology to implement unattended inspection, simplifying inspection and reducing manual workload.
New technologies are introduced to provide 24/7 monitoring.
Accurately identifies indicator status and switch status on power distribution panels to provide warnings in advance.
Identifies exceptions such as battery leakage and swelling to facilitate prompt handling.
Image recognition
New technologies help implement noise reduction, feature extraction, and exception identification in real time.
Intelligently identifies abnormal sounds of equipment and locates causes (for example, dirty or blocked UPS fans and foreign object intrusion).
Sound recognition
DCIM
Image recognition
Sound recognition
Controller
Power supply and distribution equipment
Scheduled automatic inspection
Automatic report generation

## Slide 20: Intelligent O&M - Proactive Energy Saving
Problem recognition
Result evaluation
Solution
Target baseline
Energy efficiency
components
Surveillance
Diagnosis
Adjustment
Optimization
DCIM promotes surveillance, diagnosis, adjustment and optimization of data center energy efficiency, continuously reducing energy consumption.
  The DCIM automatically optimize chilled water systems and proactively reduces the PUE.
  End-to-end visualization and diagnosis of energy efficiency allow users to identify PUE exceptions and determine energy saving improvement directions.
PLC for chiller plant teamwork (cerebellum)
Management platform (brain)
AC Teamwork (cerebellum)
Proactive Energy Saving
Notes: PLC: Programmable Logic Controller.

## Slide 21
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process
  DCIM Planning Considerations
  DCIM Planning Principles
  DCIM Planning Process

## Slide 22: DCIM Planning Considerations (1)
Two major considerations for DCIM are industry standards and O&M objectives.
Major DCIM planning considerations
Industry standards
According to selected rating criteria, the
availability design of the DCIM system
should be greater than or equal to the
availability level of data center
infrastructure.
Equipment rooms for different services in
the same data center should be designed
based on different availability according
to their importance. Corresponding
management systems should also match
the design.
O&M objectives
O&M objectives of a data center must be
considered in the planning and construction
phase. As the DCIM is the main platform
and tool for data center O&M, its planning
and design should also match the O&M
objectives.

## Slide 23: DCIM Planning Considerations - Industry Standards
According to the Uptime Institute Date Center Site Infrastructure Tier Standard, data centers are classified into four levels: Tier Ⅰ, Tier Ⅱ, Tier Ⅲ and Tier Ⅳ, which are in ascending order.
Uptime | Redundancy | Performance Requirements - Uptime
Tier Ⅳ | Fault tolerant | A Tier Ⅳ data center has multiple independent redundant equipment and paths that are physically isolated from each other. All facilities and paths work concurrently, eliminating single points of failure. All computers have dual power supplies and are connected based on the site topology. Its cooling system also requires uninterrupted operation.
Tier Ⅲ | Equipment and path redundancy | A Tier Ⅲ data center has redundant equipment and paths. All computers have dual power supplies and are connected based on the site topology. Tier III requires that only one path be used at any time.
Tier Ⅱ | Redundancy | A Tier Ⅱ data center has redundant equipment, but they are connected by a single path.
Tier Ⅰ | Meets basic requirements | A Tier Ⅰ data center meets basic requirements for data center running and has no redundancy.
Notes: The availability design of systems must match the availability level of data center infrastructure. The availability design of the DCIM system should be greater than or equal to the availability level of the data center infrastructure.
Redundancy: Some or all components of the system are repeatedly configured. When a fault occurs in the system, the redundant components take over the work of the faulty components, thereby prolonging the mean time between failures (MTBF) of the system.
Fault tolerance: There are two or more systems. At least one system is working properly at the same time. The infrastructure configured based on the fault tolerance system can still meet basic requirements for the normal running of electronic information equipment after a serious equipment fault or misoperation.

## Slide 24: DCIM Planning Considerations - O&M Objectives
Data Center Site Infrastructure Tier Standard: Operational Sustainability released by Uptime Institute illustrates O&M management objectives as follows:
  It is recommended that O&M objectives be incorporated into project design, construction, commissioning, and operations to ensure full realization and implement the objectives throughout the entire O&M life cycle of the data center. Good O&M objectives help achieve the full performance potential of the installed infrastructure.
Notes: Data center infrastructure O&M teams should discuss with the owner management, IT department, and related business departments to determine O&M management objectives. O&M management objectives can be set for different levels of data center infrastructure based on availability objectives of different applications.

## Slide 25: DCIM Considerations (2)
In addition to the main considerations, DCIM planning can also consider data center types and scales based on actual usage.
Data center types:
  Currently, data centers are classified into two types by service objects: enterprise data centers (EDCs) and Internet data centers (IDCs).
  DCIM system planning varies depending on data center types. The architecture and functions of the DCIM system must be planned and designed pertinently.
    EDC DCIM features: small and large scales, and pyramid hierarchy.
    IDC DCIM features: small scale and commercial operation.
Provincial data centers 1–n
Headquarter data centers
Municipal data centers 1–n
Branch data centers or equipment rooms 1–n
EDC DCIM pyramid hierarchy
IDC
…
Building 1
Building n
Equipment room 1
…
Smart module 1
…
Smart module n
…
Equipment room n
…
Common IDC DCIM deployment modes
Notes: EDC features:
  EDCs include data centers of enterprises and institutions such as finance, electric power, oil, and research institutes, and government data centers. EDCs are constructed, managed, and used by organizations, and use self-built or leased network resources to form a relatively closed private wide area network (WAN) (also called internal network) to provide an information-based support platform for services and management of the respective organizations. One or more data centers can be deployed based on the service scale. Data centers can be deployed in a centralized or hierarchical manner.
  An organization can have a data center. A large organization usually has multiple data centers that are distributed in different regions and has certain management relationships because its services or management scopes cover the whole country or even the world. Based on the management architecture (decision-making layer, management layer, execution layer), EDCs can be classified into data centers, sub-data centers, level-1 data centers, level-2 data centers, level-3 data centers ...
  An EDC of a large organization is usually deployed in a pyramid hierarchy to match the organization management architecture. Data centers in a lower level are more in number with a smaller scale.

## Slide 26
Notes: IDC features:
  For enterprises, IDCs lease software and hardware resources related to data centers, such as equipment room sites, networks, storage, and computing resources, to make profits. They also provide infrastructure-as-a-service (laaS), such as IT equipment hosting, and value-added services, such as IT system running monitoring, maintenance, and O&M management.
  For mass market customers, IDCs provide Internet-based information services. Currently, there are two types of enterprises that have IDCs in China. One type is telecommunication operators that have (wired and wireless) network resources, and the other type is third-party IDC service providers.

## Slide 27: DCIM Planning Considerations (3)
Data center scales:
  A larger data center has more objects to manage and requires stronger processing capability of the DCIM system.
  Attendance modes vary depending on the data center scale. The attendance mode also affects the DCIM planning and design of a data center.
Small data centers (less than 200 m2)
Medium data centers (200–500 m2)
Medium and large data centers (500–2000 m2)
Large data centers (2000–10,000 m2)
Ultra-large data centers (greater than 10,000 m2)
By area
Data Center Scale | Attendance Mode | Recommended DCIM Configuration
Ultra-large | 24/7 attendance | In addition to basic functions, functions related to attendance and routine O&M must be configured, such as remote alarm notification, mobile O&M, and electronic inspection.
Large | 24/7 attendance | 
Medium and large | 24/7 attendance | 
Medium | 24/7 attendance (recommended) | In addition to basic functions, functions related to attendance and routine O&M should be configured, such as remote alarm notification, mobile O&M, and electronic inspection.
Small | No requirement | Basic functions can be used.
Notes: Generally, ultra-large and large IDCs are used. An ultra-large or large data center consists of multiple buildings. Each building contains multiple equipment rooms, and each equipment room contains multiple smart modules, virtual equipment rooms, and cabinets. The minimum management domain of objects managed by DCIM can be an U space of a cabinet.
An ultra-large data center can consist of multiple buildings. Each building contains multiple equipment room modules, and each equipment room contains multiple smart modules, virtual equipment rooms, and rows. The minimum management domain of data center monitoring management can be a cabinet.
An ultra-large data center consisting of multiple equipment rooms can consist of equipment rooms of different levels. This meets users' requirements for different availability levels with reasonable construction and O&M costs.
Micro and small data centers are mainly access layer equipment rooms (such as equipment rooms of banks, securities outlets, and service offices of government departments) and aggregation-layer equipment rooms of organizations.
Attendance modes: Based on the importance and operation management costs of data centers, onsite attendance is not arranged for independent small and ultra-small equipment rooms. For medium data centers, onsite attendance is arranged based on service requirements. 24/7 attendance is arranged for data center clusters, ultra-large and large data centers that are managed online.

## Slide 28
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process
  DCIM Planning Considerations
  DCIM Planning Principles
  DCIM Planning Process

## Slide 29: DCIM Planning Principles
01
02
03
04
05
After a data center is put into use, the DCIM system is the core of data center infrastructure management. In addition to matching appropriate industry standards and O&M objectives, the DCIM system planning must comply with the following principles:
Applicability
Advancement
Reliability
Flexibility
Commonality
Notes: Applicability: Mature and stable products or solutions should be used.
Advancement: High-value new technologies are used to ensure that the system can keep technologically advanced and have good scalability in a certain period of time to meet requirements for future technology upgrade.
Reliability: To ensure service continuity, the system must have extremely high physical and network security and reliability.
Flexibility: The system capacity and processing capability can be easily expanded based on development requirements. In addition to supporting the access of multiple monitored objects, the system can be flexibly and quickly adjusted based on capacity expansion requirements to implement quick deployment.
Commonality: The system must use interfaces and protocols that are commonly used in China or around the world. A unified platform should be used to support cluster or distributed network architecture and multi-level management, and should feature integration, development, and scalability.

## Slide 30
DCIM System Overview
Relationship Between DCIM, Power and Environment Monitoring System, BMS, and ITSM
DCIM Development Trend
DCIM Planning Process
  DCIM Planning Considerations
  DCIM Planning Principles
  DCIM Planning Process

## Slide 31: DCIM Management and Planning Objectives
Achieves maximal availability of a data center with minimal operating costs.
DCIM management objectives
DCIM system planning objectives
After the DCIM system is planned and implemented, the system can perform all-round real-time monitoring and management on data center infrastructure. Based on monitoring information, it performs unified information-based management on the infrastructure running, thereby implementing scientific management on a data center and improving management accuracy and efficiency.
Achieves maximal availability of a data center with minimal operating costs.

## Slide 32: DCIM Planning Process
After considering factors and principles that affect DCIM planning, specify planning objectives and complete the system planning by referring to the following basic process of DCIM.
03
02
01
Requirement analysis
Perform comprehensive analysis based on users’ O&M objectives, standard requirements, critical infrastructure system, data center type, and data center scale to determine an appropriate DCIM system.
System planning
Equipment selection
Plan the DCIM architecture, functions, and performance based on requirement analysis, planning considerations and principles.
Select proper hardware for the system based on basic hardware attributes, reliability, and flexibility.

## Slide 33
DCIM concept
Relationship between DCIM and traditional power and environment monitoring, BMS, and ITSM
DCIM development trend
DCIM planning considerations and process

## Slide 34
(T or F) Compared with the traditional power and environment monitoring system, the DCIM system is more comprehensive and provides data association and analysis capabilities, implementing unified and efficient management. ( )
Notes: Answer:
  A.

## Slide 36
Chencheng/Cwx711226
2020/06.01