## Slide 1
Datacom
General
V1.0
He Junjian/WX580230
2020.02.15
Li Xianzhi/00354681
New
Ren Jie/WX504966
2020.02.15
He Junjian/WX580230
New
Lu Yueyue/WX445705
2020.06.15
Zhu Shigeng/00261992
Update
Lu Yueyue/WX445705
2021.09.15
He Junjian/WX580230
Update

## Slide 2: Advanced IGP Features

## Slide 3
Both Open Shortest Path First (OSPF) and Intermediate System to Intermediate System (IS-IS) are link-state-based Interior Gateway Protocols (IGPs). Routers that run them synchronize link state databases (LSDBs) and use the shortest path first (SPF) algorithm to calculate optimal routes.
In response to network topology changes, OSPF and IS-IS support multiple fast convergence and protection mechanisms, which minimize traffic loss caused by network faults.
To control the size of a routing table, OSPF and IS-IS support route selection and routing information control.
This course describes the advanced features of OSPF and IS-IS, including fast convergence, routing control, and other features.

## Slide 4
On completion of this course, you will be able to:
  Describe various fast convergence techniques of OSPF and IS-IS.
  Perform configurations for OSPF and IS-IS equal-cost routes.
  Configure OSPF and IS-IS to advertise default routes.
  Describe the application scenarios of OSPF and IS-IS multi-process.
  Describe graceful restart (GR) and non-stop routing (NSR) fundamentals of OSPF and IS-IS.
  Describe the application scenarios of OSPF forwarding addresses (FAs).
  Describe the fundamentals of IS-IS LSP fragment extension.

## Slide 5
OSPF Fast Convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 6: Overview of OSPF Fast Convergence
OSPF fast convergence is an extended feature of OSPF to speed up route convergence. It features partial route calculation (PRC) and the intelligent timer.
In addition, OSPF supports fast convergence upon fault rectification. For example, OSPF IP fast reroute (FRR) can be used to implement fast traffic switchover to a backup link, and OSPF can also be associated with BFD to implement fast fault detection.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 7: PRC
PRC only calculates routes that have been changed on a network.
PRC does not calculate nodes. Instead, it updates routes based on the shortest path tree (SPT) calculated using the SPF algorithm.
In route calculation, a node represents a router, and a leaf represents a route. PRC processes only the changed leaf information.
Scenario description:
  OSPF runs on a network. The figure shows the SPT with R1 as the root after network convergence. When R1 accesses R5, traffic is sent to the destination based on [outbound interface of R1's downlink, IP address of R3's uplink interface].
  OSPF is enabled on Loopback0 of R5. This means that a new network segment is added to the OSPF network.
PRC:
  R5 floods a new LSA on the entire network.
  After receiving the LSA, R1 creates a new route that inherits the original path and next hop used when R1 accesses R5. In this case, the SPT remains unchanged, and only a leaf is added to R5.
  Therefore, when R1 accesses Loopback0 of R5, traffic is sent to the destination based on [outbound interface of R1's downlink, IP address of R3's uplink interface].
Benefits:
  PRC focuses only on routes that are changed due to the addition of network segments to an OSPF network, thereby speeding up route calculation.
Loopback0: A directly connected network segment is added.
R1 (root)
R2
R3
R4
R5
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Note: On Huawei devices, OSPF PRC is enabled by default.

## Slide 8: Intelligent Timer
The intelligent timer is used for SPF calculation and LSA generation.
It can quickly respond to a small number of external incidents and prevent excessive CPU consumption.
Controlling LSA Generation and Reception
To prevent network connections or frequent route flapping from consuming excessive device resources, OSPF complies with the following rules:
After an LSA is generated, it cannot be generated again within 1s. The interval for updating LSAs is 5s.
The interval for receiving LSAs is 1s.
On a stable network where routes need to be fast converged, the intelligent timer can be used to set the interval for updating LSAs to 0s in order to cancel this interval. In this manner, topology or route changes can be immediately advertised to the network through LSAs or be immediately detected, thereby speeding up route convergence on the network.
Controlling Route Calculation
When a network changes, the OSPF LSDB changes, and the shortest path needs to be recalculated. If a network changes frequently, the shortest path is calculated accordingly, which results in excessive consumption of system resources and compromises device efficiency.
You can configure the intelligent timer to set a proper interval for SPF calculation in order to prevent excessive consumption of a router's memory and bandwidth resources.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: If the interval for triggering route calculation is long, the network convergence speed is affected.
The first timeout period of the intelligent timer is fixed. Before the intelligent timer expires, if an event that triggers the timer occurs, the next timeout period of the intelligent timer becomes longer.

## Slide 9: Basic Intelligent Timer Configuration Commands (1)
After the intelligent timer is used:
  The initial interval for updating LSAs is specified by start-interval.
  The interval at which LSAs are updated for the nth (n ≥ 2) time equals hold-interval x 2(n – 2).
  When the interval specified by hold-interval x 2(n – 2) reaches the maximum interval specified by max-interval, OSPF updates LSAs at the maximum interval for three consecutive times. Then, OSPF returns to the first step and updates LSAs at the initial interval specified by start-interval.
[Huawei-ospf-1] lsa-originate-interval { 0 | { intelligent-timer max-interval start-interval hold-interval | other-type interval } }
Set an interval for updating OSPF LSAs.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval at which LSAs are updated are 5000 ms, 500 ms, and 1000 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf] lsa-originate-interval { 0 | { intelligent-timer max-interval start-interval hold-interval | other-type interval } }
  0: sets the interval for updating LSAs to 0s, that is, cancels the interval of 5s for updating LSAs.
  intelligent-timer: uses the intelligent timer to set the update interval for router-LSAs and network-LSAs.
  max-interval: specifies the maximum interval for updating OSPF LSAs. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 5000.
  start-interval: specifies the initial interval for updating OSPF LSAs. The value is an integer ranging from 0 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for updating OSPF LSAs. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 1000.
  other-type: sets an update interval for OSPF LSAs except router-LSAs and network-LSAs.
  interval: specifies the interval for updating LSAs. The value is an integer ranging from 0 to 10, in seconds. The default value is 5.

## Slide 10: Basic Intelligent Timer Configuration Commands (2)
After the intelligent timer is used:
  The initial interval for receiving LSAs is specified by start-interval.
  The interval at which LSAs are received for the nth (n ≥ 2) time equals hold-interval x 2(n – 2).
  When the interval specified by hold-interval x 2(n – 2) reaches the maximum interval specified by max-interval, OSPF receives LSAs at the maximum interval for three consecutive times. Then, OSPF returns to the first step and receives LSAs at the initial interval specified by start-interval.
[Huawei-ospf-1] lsa-arrival-interval { interval | intelligent-timer max-interval start-interval hold-interval }
Set an interval for receiving OSPF LSAs.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval at which LSAs are received are 1000 ms, 500 ms, and 500 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf-1] lsa-arrival-interval { interval | intelligent-timer max-interval start-interval hold-interval }
  interval: specifies the interval for receiving LSAs. The value is an integer ranging from 0 to 10000, in milliseconds.
  intelligent-timer: uses the intelligent timer to set the receive interval for LSAs.
  max-interval: specifies the maximum interval for receiving OSPF LSAs. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 1000.
  start-interval: specifies the initial interval for receiving OSPF LSAs. The value is an integer ranging from 0 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for receiving OSPF LSAs. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 500.

## Slide 11: Basic Intelligent Timer Configuration Commands (3)
After the intelligent timer is used, the interval for SPF calculation is as follows:
  The initial interval for SPF calculation is specified by start-interval.
  The interval for SPF calculation for the nth (n ≥ 2) time equals hold-interval x 2(n – 2)..
  When the interval specified by hold-interval x 2(n – 2). reaches the maximum interval specified by max-interval, OSPF performs SPF calculation at the maximum interval for three consecutive times. Then, OSPF returns to the first step and performs SPF calculation at the initial interval specified by start-interval.
[Huawei-ospf-1] spf-schedule-interval { interval1 | intelligent-timer max-interval start-interval hold-interval | millisecond interval2 }
Set an interval for OSPF route calculation.
By default, the intelligent timer is enabled; the maximum interval, initial interval, and hold interval for SPF calculation are 10000 ms, 500 ms, and 1000 ms, respectively.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Command: [Huawei-ospf-1] spf-schedule-interval { interval1 | intelligent-timer max-interval start-interval hold-interval | millisecond interval2 }
  interval1: specifies an interval for OSPF SPF calculation. The value is an integer ranging from 1 to 10, in seconds.
  intelligent-timer: uses the intelligent timer to set the interval for OSPF SPF calculation.
  max-interval: specifies the maximum interval for OSPF SPF calculation. The value is an integer ranging from 1 to 120000, in milliseconds. The default value is 10000.
  start-interval: specifies the initial interval for OSPF SPF calculation. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 500.
  hold-interval: specifies the hold interval for OSPF SPF calculation. The value is an integer ranging from 1 to 60000, in milliseconds. The default value is 1000.
  millisecond interval2: specifies an interval for OSPF SPF calculation. The value is an integer ranging from 1 to 10000, in milliseconds.

## Slide 12: OSPF IP FRR
OSPF IP fast reroute (FRR) is a dynamic IP FRR technology that uses the loop-free alternate (LFA) algorithm to pre-calculate a backup path and saves it in the forwarding table. If the primary link fails, traffic is rapidly switched to the backup link, ensuring traffic continuity and achieving traffic protection. OSPF IP FRR can reduce the fault recovery time to less than 50 ms.
The LFA algorithm calculates a backup link based on the following principles:
  A device uses the SPF algorithm to calculate shortest paths to the destination, with each neighbor that provides a backup link as a root node. The device then uses the inequality to calculate a loop-free backup link with the minimum cost.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 13: Networking of OSPF IP FRR
OSPF IP FRR protects traffic against either a link failure or a node-and-link failure.
Link protection
Link protection inequality:
Distance_opt (N, D) < Distance_opt (N, S) + Distance_opt (S, D)
This ensures that the traffic from node N to node D does not pass through node S. That is, this ensures that no loop occurs.
S
Cost = 10
Cost = 5
Cost = 10
Cost = 5
N
R1
D
Node-and-link protection
Link protection inequality:
Distance_opt (N, D) < Distance_opt (N, S) + Distance_opt (S, D)
Node protection inequality:
Distance_opt (N, D) < Distance_opt (N, E) + Distance_opt (E, D)
This ensures that the traffic from node N to node D does not pass through nodes S and E. That is, this ensures that no loop occurs.
S
Cost = 10
Cost = 5
Cost = 10
Cost = 5
N
E
D
S: source node
D: destination node
N: node along the backup link
Distance_opt (X, Y)
indicates the shortest path from node X to node Y.
S: source node
D: destination node
N: node along the backup link
E: faulty node
Traffic flows from node S to node D. The link cost satisfies the link protection inequality. If the primary link fails, node S switches the traffic to the backup link. This ensures that the traffic interruption time is less than 50 ms.
Node-and-link protection must meet the preceding two inequalities.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Node-and-link protection:
  As shown in the right figure, traffic flows from node S to node D. The link cost satisfies the node-and-link protection inequality. If the primary link fails, node S switches the traffic to the backup link. This ensures that the traffic interruption time is less than 50 ms.
OSPF IP FRR protects traffic against either a link failure or a node-and-link failure.
  Link protection takes effect when the traffic to be protected flows along a specified link.
  Node-and-link protection takes effect when the traffic to be protected flows along a specified device. Node-and-link protection takes precedence over link protection.

## Slide 14: Basic OSPF IP FRR Configuration Commands
[Huawei-ospf-1] frr
[Huawei-ospf-1-frr]
Enable OSPF IP FRR.
Create OSPF FRR and enter its view.
[Huawei-ospf-1-frr] loop-free-alternate
After OSPF IP FRR is enabled, the device uses the LFA algorithm to calculate the next hop and outbound interface for a backup link.
[Huawei-GigabitEthernet0/0/1] ospf frr block
(Optional) Disable OSPF IP FRR on an interface.
OSPF IP FRR can be disabled on an interface of a specific device that is running important services and resides on an FRR backup link. This setting prevents the device connected to this interface from being a part of a backup link and being burdened after FRR switches traffic to the backup link.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 15: Example for Configuring OSPF IP FRR
OSPF
area 0
R1
Cost = 10
Cost = 5
Cost = 10
Cost = 5
R2
R3
R4
GE0/0/1
GE0/0/2
GE0/0/1
If the link between R1 and R3 fails, traffic forwarded by R1 can be quickly switched to the backup link and forwarded by R2.
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/0 | 10.1.13.1/24
 |  | GE0/0/1 | 10.1.12.1/24
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24
 |  | GE0/0/2 | 10.1.23.2/24
R3 | 10.1.3.3 | GE0/0/0 | 10.1.13.3/24
 |  | GE0/0/1 | 10.1.34.3/24
 |  | GE0/0/2 | 10.1.23.3/24
R4 | 10.1.4.4 | GE0/0/1 | 10.1.34.4/24
1. Assign an IP address to each interface and configure OSPF on each device. (The configuration details are not provided here.)
[R1] interface GigabitEthernet 0/0/0
[R1-GigabitEthernet 0/0/0] ospf cost 10
[R1-GigabitEthernet 0/0/0] quit
[R1] interface GigabitEthernet 0/0/1
[R1-GigabitEthernet 0/0/1] ospf cost 10
[R1-GigabitEthernet 0/0/1] quit
2. Configure an OSPF cost for each device. The following example uses the command output on R1.
The cost configurations of R2, R3, and R4 are similar to the configuration of R1.
GE0/0/0
3. Enable OSPF IP FRR on R1.
[R1] ospf
[R1-ospf-1] frr
[R1-ospf-1-frr] loop-free-alternate
[R1-ospf-1-frr] quit
[R1-ospf-1] quit
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 16: Checking the OSPF IP FRR Configuration
OSPF
area 0
R1
Cost = 10
Cost = 5
Cost = 10
Cost = 5
R2
R3
R4
GE0/0/1
GE0/0/2
GE0/0/1
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/0 | 10.1.13.1/24
 |  | GE0/0/1 | 10.1.12.1/24
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24
 |  | GE0/0/2 | 10.1.23.2/24
R3 | 10.1.3.3 | GE0/0/0 | 10.1.13.3/24
 |  | GE0/0/1 | 10.1.34.3/24
 |  | GE0/0/2 | 10.1.23.3/24
R4 | 10.1.4.4 | GE0/0/1 | 10.1.34.4/24
GE0/0/0
Check information about the route from R1 to GE0/0/1 of R4.
[R1]display ospf routing 10.1.34.4
OSPF Process 1 with Router ID 10.1.1.1
Destination : 10.1.34.0/24
AdverRouter : 10.1.4.4 Area : 0.0.0.0
Cost : 15 Type : Transit
NextHop : 10.1.13.3 Interface : GigabitEthernet0/0/0
Priority : Low Age : 00h01m59s
Backup Nexthop : 10.1.12.2 Backup Interface:GigabitEthernet0/0/1
Backup Type : LFA LINK
You can find that OSPF generates a backup link after OSPF IP FRR is enabled on R1.
Overview
PRC
Intelligent Timer
FRR
BFD Association

## Slide 17: BFD for OSPF
A link fault or a topology change causes devices to recalculate routes. Fast and efficient routing protocol convergence is necessary to improve network availability.
BFD for OSPF associates BFD with OSPF. If a fault occurs on the link between a device and its neighbor, BFD can rapidly detect the link fault to speed up OSPF's response to network topology changes.
OSPF
BFD
The working principle of BFD for OSPF is as follows:
  OSPF neighbor relationships are established between R1, R2, and R3. When the neighbor relationships enter the Full state, BFD is instructed to set up a BFD session.
  If a fault occurs on the link between R1 and R2, BFD detects the fault and notifies R1. R1 processes the BFD session down event and recalculates the route. The new path is R1-R3-R2.
R1
R3
S1
R2
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: OSPF periodically sends Hello packets to neighbors to detect faults. It takes more than 1s to detect a fault. By default, when the OSPF Dead timer expires, the neighbor is considered invalid. The default value of the OSPF Dead timer is 40s. With the development of technologies, voice, video, and video on demand (VOD) services are widely used. These services are sensitive to the packet loss rate and delay. When the traffic rate reaches gigabit per second (Gbit/s), long-time fault detection causes a large number of packets to be lost. This cannot meet high reliability requirements of the carrier-class network.
BFD for OSPF is introduced to resolve this problem. After BFD for OSPF is configured in a specified process or on a specified interface, the link status can be rapidly detected and fault detection can be completed in milliseconds. This speeds up OSPF convergence when the link status changes.

## Slide 18: Basic BFD for OSPF Configuration Commands
[Huawei-ospf-1] bfd all-interfaces enable
Configure BFD for OSPF.
Enable BFD in an OSPF process.
[Huawei-ospf-1] bfd all-interfaces { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
Configure BFD session parameters.
[Huawei-GigabitEthernet0/0/1] ospf bfd enable
Configure BFD on a specified interface.
Enable BFD on an OSPF interface.
[Huawei-GigabitEthernet0/0/1] ospf bfd { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
Configure BFD session parameters on the OSPF interface.
Overview
PRC
Intelligent Timer
FRR
BFD Association
Notes: Prerequisites:
  Before using BFD to quickly detect link faults, run the bfd command in the system view to enable BFD globally.
The BFD configuration on an interface takes precedence over that in a process. If BFD is enabled on an interface, the BFD parameters on the interface are used to establish BFD sessions.
OSPF IP FRR can be associated with BFD.
  During the OSPF IP FRR configuration, the underlying layer needs to fast respond to a link status change so that traffic can be switched to the backup link immediately.
  OSPF IP FRR and BFD can be bound to rapidly detect link faults. This ensures that traffic is rapidly switched to the backup link in the case of link failures.
Command: [Huawei-ospf-1] bfd all-interfaces { min-rx-interval receive-interval | min-tx-interval transmit-interval | detect-multiplier multiplier-value | frr-binding }
  min-rx-interval receive-interval: specifies an expected minimum interval for receiving BFD packets from the peer. The value is an integer ranging from 10 to 2000, in milliseconds. The default value is 1000.
  min-tx-interval transmit-interval: specifies a minimum interval for sending BFD packets to the peer. The value is an integer ranging from 10 to 2000, in milliseconds. The default value is 1000.
  detect-multiplier multiplier-value: specifies a local detection multiplier. The value is an integer ranging from 3 to 50. The default value is 3.
  frr-binding: binds the BFD session status to the link status of an interface. If a BFD session goes down, the physical link of the bound interface also goes down, triggering traffic to be switched to the backup link.

## Slide 19
OSPF Fast Convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 20: Overview of OSPF Route Control
OSPF route control includes:
  Adjusting the OSPF interface cost
  Setting the maximum number of equal-cost routes for load balancing
  Importing external routes
  Configuring route summarization
  Configuring default route advertisement
  Configuring filter-policies
  Configuring OSPF to filter outgoing LSAs
  Configuring an ABR to filter Type 3 LSAs
  Setting the maximum number of External LSAs in the LSDB
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: This course describes only equal-cost routes, default routes, and LSA filtering. For other information, see HCIP-Datacom-Core Technology.

## Slide 21: Equal-Cost Route
If the destinations and costs of the multiple routes discovered by one routing protocol are the same, these routes are equal-cost routes and can participate in load balancing.
The device sends packets to the same destination address through multiple equal-cost routes in load balancing mode.
Set the maximum number of equal-cost routes for load balancing.
[Huawei-ospf-1] maximum load-balancing number
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-ospf-1] maximum load-balancing number
  number: specifies the maximum number of equal-cost routes for load balancing. The value range varies according to the device model. For details, see the product documentation of the corresponding device.

## Slide 22: Example for Configuring the Number of Equal-Cost Routes for Load Balancing
It is required that R1 can access the loopback interface address of R3 through the path R1 -> R3 or the path R1 -> R2 -> R3.
OSPF
Area 0
R1
Cost = 10
Cost = 5
Cost = 5
R3
GE0/0/0
GE0/0/1
GE0/0/2
R2
Device | Interface | IP Address
R1 | GE 0/0/0 | 10.1.13.1/24
 | GE 0/0/1 | 10.1.12.1/24
R2 | GE 0/0/1 | 10.1.12.2/24
 | GE 0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE 0/0/0 | 10.1.13.3/24
 | GE 0/0/2 | 10.1.23.3/24
1. Assign an IP address to each interface and configure OSPF on each device. (Details are not provided here.)
[R1] ospf
[R1-ospf-1] maximum load-balancing 2
2. Configure the maximum number of OSPF equal-cost routes for load balancing on R1.
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 OSPF 10 10 D 10.1.13.3 GigabitEthernet0/0/0
OSPF 10 10 D 10.1.12.2 GigabitEthernet0/0/1
3. Verify the configuration.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 23: Default Route
On the area border and AS border of an OSPF network generally reside multiple routers for egress backup or traffic load balancing. In this case, a default route can be configured to reduce the number of routing entries in the routing table and ensure high availability of the network.
OSPF default routes are generally applied to the following scenarios:
  An ABR advertises Type 3 LSAs carrying the default route so that routers in an area forward inter-area packets accordingly.
  An ASBR advertises Type 5 or Type 7 LSAs carrying the default route so that routers in an AS forward AS-external packets.
Area Type | Trigger Condition | Advertised by | LSA Type | Flooding Scope
Common area | The default-route-advertise command is run. | ASBR | Type 5 LSA | Common area
Stub area and totally stubby area | Automatically generated | ABR | Type 3 LSA | Stub area
NSSA | The nssa [ default-route-advertise ] command is run. | ASBR | Type 7 LSA | NSSA
Totally NSSA | Automatically generated | ABR | Type 3 LSA | NSSA
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Default routes have all 0s as the destination address and mask. A device uses a default route to forward packets when no matching route is available. Hierarchical management of OSPF routes prioritizes the default route carried in Type 3 LSAs over the default route carried in Type 5 or Type 7 LSAs.
Common area:
  By default, routers in a common OSPF area do not generate default routes. To enable a router in a common OSPF area to advertise a default route to OSPF, run the default-route-advertise command on the router. After the command is run, the router generates a default ASE LSA (Type 5 LSA) and advertises it to the entire OSPF AS.
Stub area:
  Type 5 LSAs cannot be advertised within a stub area. All routers within a stub area can learn AS external routes only through an ABR.
  The ABR in a stub area automatically generates a default Type 3 LSA and advertises it to the entire stub area. The ABR uses the default route to divert traffic destined for a destination outside the AS to itself and then forwards the traffic.

## Slide 24
Notes: Totally stub area:
  Neither Type 3 nor Type 5 LSAs can be advertised within a totally stub area. All routers within a totally stub area can learn AS external routes and other areas' routes only through an ABR.
  The ABR in a totally stub area automatically generates a default Type 3 LSA and advertises it to the entire stub area. The ABR uses the default route to divert traffic destined for a destination outside the AS to itself and then forwards the traffic.
NSSA:
  To enable packets destined for routers outside an AS to be sent by way of an ASBR in an NSSA, and other packets destined for routers outside the AS to be sent by way of an ABR in the NSSA, configure the ABR to generate a default Type 7 LSA and advertise this LSA within the entire NSSA. In this case, a default Type 7 LSA will be generated on the ABR, regardless of whether the default route 0.0.0.0 exists in the routing table.
  To enable all packets destined for routers outside the AS to be sent by way of an ASBR in the NSSA, run the nssa [default-route-advertise] command on the ASBR so that the ASBR generates a default NSSA LSA (Type 7 LSA) and advertises it to the entire NSSA. In this case, a default Type 7 LSA is generated only when the default route 0.0.0.0 exists in the routing table on the ASBR.
  Note: Default routes are flooded only within the local NSSA and are not flooded within the entire OSPF AS. If routers in the local NSSA have no routes to the outside of the AS, the routers can forward packets outside of the AS through an ASBR. However, packets of other OSPF areas cannot be sent outside the AS through this ASBR. An ABR does not translate default Type 7 LSAs into default Type 5 LSAs for flooding in the entire AS.
Totally NSSA:
  The ABR in a totally NSSA automatically advertises the default route through a Type 3 LSA to the NSSA. The ASBR in a totally NSSA, however, does not automatically advertise default routes. In this scenario, the routers in the area can reach the corresponding external network segments through the external routes imported by the ASBR and reach other network segments through the default routes delivered by the ABR.
  If you want routers in a totally NSSA to select an ASBR (rather than an ABR) as the default egress, you need to configure the ASBR to deliver the default route.

## Slide 25: Configuring Default Route Advertisement to OSPF Areas
Note:
  The import-route (OSPF) command cannot import the default route of another routing protocol. To enable a router to advertise the default route of another routing protocol, run the default-route-advertise command on an ASBR so that the default route is advertised to all common OSPF areas.
  Before advertising a default route, OSPF compares the preferences of default routes in an OSPF area and then advertises a default route with the highest preference. If a static default route is configured on an OSPF device, ensure that the preference of the static default route is lower than that of the default route to be advertised by OSPF. This ensures that the default route advertised by OSPF will be added to the routing table of the OSPF device.
[Huawei-ospf-1] default-route-advertise [ [ always | permit-calculate-other ] | cost cost | type type | route-policy route-policy-name [ match-any ] ]
Configure default route advertisement to common OSPF areas.
By default, OSPF devices in a common OSPF area do not generate default routes.
[Huawei-ospf-1] default-route-advertise summary cost cost
Configure default route advertisement through a Type 3 summary LSA and set a cost for the route.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-ospf-1] default-route-advertise [[always | permit-calculate-other] | cost cost | type type | route-policy route-policy-name [match-any]]
  always: An LSA that describes the default route is generated and advertised regardless of whether the local device has an active default route that does not belong to the current OSPF process.
    If always is configured, the device does not calculate the default routes from other devices.
    If always is not configured, an LSA that describes the default route can be generated only if an active default route that does not belong to the current OSPF process exists in the routing table of the local device.
  permit-calculate-other: An LSA that describes the default route is generated and advertised only if the device has an active default route that does not belong to the current OSPF process, and the device still calculates the default routes from other devices.
  type type: specifies the type of an external route. The value is 1 or 2. The default value is 2.
    1: Type 1 external route
    2: Type 2 external route
  route-policy route-policy-name: specifies the name of a route-policy. The device advertises default routes according to the configuration of the route-policy when the routing table of the device contains a default route that matches the route-policy but does not belong to the current OSPF process. The value is a string of 1 to 40 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").

## Slide 26
Notes:   match-any: The device advertises default routes according to the configuration of the route-policy when the routing table contains routes that match the route-policy.
Command: [Huawei-ospf-1] default-route-advertise summary cost cost
  summary: Advertises the Type 3 summary LSA of the specified default route. Before specifying this parameter, ensure that a VPN is enabled. Otherwise, routes cannot be advertised.
  cost cost: specifies the cost of the LSA. The value is an integer ranging from 0 to 16777214. The default value is 1.
always:
  If the ASBR has a default route, the default-route-advertise command enables the ASBR to advertise the default route 0.0.0.0 to all OSPF areas.
  If the ASBR has no default route, the default-route-advertise always command or the default-route-advertise command can be used as required:
    With always configured, the ASBR can advertise the default route 0.0.0.0 even if there is no default route, and the ASBR does not calculate the default routes sent by other devices.
    Without always configured, the ASBR generates the LSA of the default route only when the local routing table contains an active default route (non-BGP route) that does not belong to the current OSPF process.
match-any:
  If a route-policy is configured with match-any, and multiple routes match the policy, a default LSA will be generated based on the optimal route. The rules for optimal route selection are as follows:
    A route configured with type takes precedence over that not configured with type. A route configured with a smaller type value takes precedence over that configured with a larger type value.
    A route configured with cost takes precedence over that not configured with cost. A route configured with a smaller cost value takes precedence over that configured with a larger cost value.
    A route configured with tag takes precedence over that not configured with tag. A route configured with a smaller tag value takes precedence over that configured with a larger tag value.

## Slide 27: Configuring OSPF to Filter Outgoing LSAs
When multiple links exist between two routers, you can enable the function to filter outgoing LSAs, preventing them from being sent to particular links. This function can help reduce unnecessary retransmission of LSAs and reduce bandwidth consumption.
Filtering the outgoing LSAs on a specified OSPF interface can prevent unwanted LSAs from being sent to neighbors, thus reducing the LSDB sizes of the neighbors and speeding up network convergence.
To filter outgoing LSAs on an OSPF interface, run the following command:
[Huawei-GigabitEthernet0/0/1] ospf filter-lsa-out { all | { summary [ acl { acl-number | acl-name } ] | ase [ acl { acl-number | acl-name } ] | nssa [ acl { acl-number | acl-name } ] } }
The command configuration does not take effect for the LSAs that have been sent out before the command is run. The aging time of such an LSA is still 3600 seconds.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [Huawei-GigabitEthernet0/0/1] ospf filter-lsa-out { all | { summary [ acl { acl-number | acl-name } ] | ase [ acl { acl-number | acl-name } ] | nssa [ acl { acl-number | acl-name } ] } }
  all: filters all outgoing LSAs, except grace LSAs.
  summary: filters outgoing network-summary-LSAs (Type 3).
  ase: filters outgoing AS-external-LSAs (Type 5).
  nssa: filters outgoing NSSA-LSAs (Type 7).
  acl acl-number: specifies the number of a basic ACL. The value is an integer ranging from 2000 to 2999.
  acl acl-name: specifies the name of an ACL. The value is a string of 1 to 32 case-sensitive characters. It cannot contain spaces and must start with a letter (a to z or A to Z).

## Slide 28: Configuring OSPF to Filter ABR Type 3 LSAs
Configure filtering policies for incoming and outgoing ABR Type 3 LSAs (network-summary-LSAs) in an area, allowing only those that pass the filtering to be sent and accepted.
Filtering Type 3 LSAs in a specified OSPF area can prevent unwanted LSAs from being sent to neighbors, thus reducing the LSDB sizes and speeding up network convergence.
To filter outgoing Type 3 LSAs in an OSPF area, run the following command:
To filter incoming Type 3 LSAs in an OSPF area, run the following command:
[Huawei-ospf-1-area-0.0.0.1] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export
[Huawei-ospf-1-area-0.0.0.1] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } import
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Command: [ Huawei-ospf-1-area-0.0.0.1 ] filter { acl-number | acl-name acl-name | ip-prefix ip-prefix-name | route-policy route-policy-name } export
  acl-number: specifies the number of a basic ACL. The value is an integer ranging from 2000 to 2999.

## Slide 29: Overview of OSPF Database Overflow
The LSDBs of OSPF devices in the same area are synchronized after routes are converged. However, achieving such a state can be difficult as the number of routes on a network continuously increases, causing some devices to be unable to carry excess routing information due to limited system resources. This is called an OSPF database overflow.
One way to solve such an issue is to configure stub areas or NSSAs, which reduces the amount of routing information on devices. However, such an approach cannot prevent an OSPF database overflow caused by a sharp increase in dynamic routes. To resolve this issue, set the maximum number of non-default external LSAs allowed in the LSDB of a device to dynamically control the LSDB size.
Set the maximum number of non-default external LSAs allowed in the LSDB.
[Huawei-ospf-1] lsdb-overflow-limit number
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: When the number of external LSAs (Type 5 and Type 7) imported by OSPF exceeds the maximum number supported, excessive external LSAs cannot be processed properly and are discarded. To address this issue, you can set a proper upper limit for the number of non-default external LSAs in the LSDB, so as to adjust and optimize the OSPF network.
Command: [Huawei-ospf-1] lsdb-overflow-limit number
  number: specifies the maximum number of non-default external LSAs allowed in the LSDB. The value is an integer ranging from 1 to 1000000.

## Slide 30: Preventive Measures for OSPF Database Overflows
Setting the maximum number of non-default external routes on a router can prevent OSPF database overflows.
Set the same maximum number for all routers on an OSPF network. When the number of non-default external routes on a router reaches the maximum number, the router enters the Overflow state and starts the Overflow state timer (default timeout period: 5s). After the timer expires, the router automatically exits the Overflow state.
Enters the Overflow state.
Stays in the Overflow state.
Exits the Overflow state.
Overflow Phase | OSPF Processing
Enters the Overflow state. | Deletes all non-default external routes generated by the router itself. Starts the Overflow state timer.
Stays in the Overflow state. | Does not generate non-default external routes. Discards newly received non-default external routes and does not reply with LSAck packets. Checks whether the number of external routes still exceeds the maximum number when the overflow state timer expires. If not, the router exits the Overflow state. If so, the router restarts the Overflow state timer.
Exits the Overflow state. | Deletes the Overflow state timer. Generates non-default external routes. Accepts newly received non-default external routes and replies with LSAck packets. Gets ready to enter the Overflow state again.
Restarts the timer.
Enters the Overflow state again.
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 31: Example for Configuring OSPF Route Control (1)
To reduce the number of LSAs on R3 and ensure that R3 can properly communicate with routers in other areas, check that the following requirements are met:
  R2 does not inject Type 3 LSAs into Area 1.
  R2 advertises default routes.
1. Assign an IP address to each interface and configure OSPF on each device. (omitted).
[R2] acl 2000
[R2-acl-basic-2000] rule deny
[R2-acl-basic-2000] quit
[R2] ospf
[R2-ospf-1] area 1
[R2-ospf-1-area-0.0.0.1] filter 2000 import
2. Configure R2 to filter Type 3 LSAs.
[R2] ospf
[R2-ospf-1] default-route-advertise always
3. Configure R2 to advertise default routes.
OSPF
R1
R2
R3
Area0
Area1
Type 3 LSA
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 32: Example for Configuring OSPF Route Control (2)
1. Check the LSDB of R3.
[R3]display ospf lsdb
OSPF Process 1 with Router ID 10.1.23.3
Link State Database
Area: 0.0.0.1
Type LinkState ID AdvRouter Age Len Sequence Metric
Router 10.1.23.3 10.1.23.3 731 48 80000004 1
Router 10.1.12.2 10.1.12.2 406 36 80000008 1
Network 10.1.23.2 10.1.12.2 730 32 80000002 0
AS External Database
Type LinkState ID AdvRouter Age Len Sequence Metric
External 0.0.0.0 10.1.12.2 406 36 80000001 1
2. Check the routing table of R3.
[R3]dis ip routing-table
Route Flags: R - relay, D - download to fib
-----------------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 9 Routes : 9
Destination/Mask Proto Pre Cost Flags NextHop Interface
0.0.0.0/0 O_ASE 150 1 D 10.1.23.2 GigabitEthernet0/0/1
……
The LSDB of R3 in Area1 does not contain Type 3 LSAs but contains a default Type 5 LSA.
R3 can access devices in other areas through the default route.
OSPF
R1
R2
R3
Area0
Area1
Type 3 LSA
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case

## Slide 33: OSPF Route Control Case Analysis
Network deployment:
  An enterprise network is divided into two networks, one for the finance department and the other for the marketing department.
  The enterprise network uses OSPF to allow internal network connectivity. The backbone network is deployed in area 0, clients of the finance department's network are deployed in area 1, and clients of the marketing department's network are deployed in area 2.
  Border devices access department servers through static routes, which are imported to the OSPF process.
Requirements:
  As long as the border-1 router and its uplink work properly, the data flows of the finance department are forwarded only through the border-1 router.
  As long as the core-1 router and its uplink work properly, the data flows of the finance department are forwarded only through the core-1 router.
  For details about the data forwarding requirements of the marketing department, see the comment of this slide.
AGG-1
Finance department client
Marketing department client
Core-1
Border-1
AGG-2
Core-2
Border-2
OSPF
Area 2
Data flow of the finance department
Static routing
Finance server
Marketing server
OSPF
Area 1
OSPF
Area 0
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Notes: Data forwarding requirements of the marketing department:
  As long as the border-2 router and its uplink work properly, the data flows of the marketing department are forwarded only through the border-2 router.
  As long as the core-2 router and its uplink work properly, the data flows of the marketing department are forwarded only through the core-2 router.
This case uses the data forwarding path of the finance department as an example. The data forwarding path of the marketing department is not described here.

## Slide 34: Requirement Analysis
Controlling the precise internal path of data flows:
  Load-balancing path should not exist.
To ensure that fixed ASBRs are used to forward data, the internal network changes must be ignored. That is, the internal route cost is not calculated.
—Use Type 2 external routes of OSPF.
Data needs to be sent to a specific ASBR along the planned path on the network.
—Adjust the internal path cost.
Controlling the network egress for data forwarding:
  Data of the finance department is always forwarded through border-1.
  Data of the marketing department is always forwarded through border-2.
AGG-1
Finance department client
Marketing department client
Core-1
Border-1
AGG-2
Core-2
Border-2
Data flow of the finance department
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server
Notes: Type 2 external route:
  Because a Type 2 external route offers low reliability, its cost is considered to be much greater than the cost of any internal route to an ASBR.
  Cost of a Type 2 external route = Cost of the route from an ASBR to the destination

## Slide 35: Traffic Egress Control
Implementation:
  Import static routes destined for the finance department server to the OSPF processes of R1 (border-1) and R2 (border-2) to implement egress backup through route-policies.
  Set the type of the imported external route to Type 2.
  On R1, set the cost of the external route to 100; on R2, set the cost of the external route to 200.
Configuration result:
  When there are two Type 2 external routes with different costs on the same network segment, the network device prefers the route with a smaller cost. In this case, each network device preferentially selects R1 as the egress.
AGG-1
Finance department client
Marketing department client
Core-1
Border-1
R1
AGG-2
Core-2
Border-2
R2
Imported finance department routes
Type: Type 2
Cost: 100
Imported finance department routes
Type: Type 2
Cost: 200
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server
Notes: The internal path cost to each ASBR is not considered during traffic egress control.

## Slide 36: Controlling Internal Paths
Network requirement analysis:
  If the network is running properly, S3 (AGG-1) selects path 1.
  If the link between S1 (core-1) and R1 fails, S3 selects path 2.
  If S1 fails, S3 selects path 3.
Implementation:
  Path 1-cost < Path 2-cost < Path 3-cost
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S3
Core-2
S2
Border-2
R2
Data flow of the finance department
1
2
3
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 37: Controlling Internal Paths: Adjusting the Cost Between Aggregation Devices and Core Devices
If the link between S1 and R1 fails, S3 preferentially selects path 1 and then path 2 because S1 is working properly.
Implementation:
  Path 1-cost < Path 2-cost, that is:
  Path 1 can be achieved by adjusting the path cost between aggregation devices and core devices.
[Cost(S3-S1) + Cost(S1-S2) + Cost(S2-R1)] < [Cost(S3-S2) + Cost(S2-R1)]
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S3
Core-2
S2
Border-2
R2
Data flow of the finance department
Cost=10
Cost=10
Cost=50
Cost=10
Cost=50
Cost=50
1
2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 38: Controlling the Internal Path: Adjusting the Cost Between Core Devices and Boundary Devices
If the link between S3 and S1 fails, S3 preferentially selects path 1 and then path 2 because S1 is working properly.
Implementation:
  Path 1-cost < Path 2-cost, that is:
  Path 1 can be preferentially selected by adjusting the path cost between core devices and boundary devices.
[Cost(S3-S2) + Cost(S2-S1) + Cost(S1-R1)] < [Cost(S3-S2) + Cost(S2-R1)]
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S3
Core-2
S2
Border-2
R2
Data flow of the finance department
Cost=10
Cost=10
Cost=50
Cost=10
Cost=50
Cost=50
1
2
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 39: Example for Configuring OSPF Route Control (1)
Import static routes to the OSPF process on R1.
Configure a route-policy on R1 and set the cost to 100.
[R1] acl 2000
[R1-acl-basic-2000] rule permit source 192.168.10.0 0.0.0.255
[R1-acl-basic-2000] quit
[R1] route-policy static2ospf permit node 10
[R1-route-policy] if-match acl 2000
[R1-route-policy] apply cost 100
[R1-route-policy] quit
[R1] route-policy static2ospf permit node 20
[R1-route-policy] quit
[R1] ospf
[R1-ospf-1] import-route static route-policy static2ospf type 2
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S4
Core-2
S2
Border-2
R2
OSPF
Area 2
Static routing
OSPF
Area 1
OSPF
Area 0
192.168.10.0/24
192.168.20.0/24
Imported finance department routes
Type: Type 2
Cost: 100
Imported finance department routes
Type: Type 2
Cost: 200
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 40: Example for Configuring OSPF Route Control (2)
Import static routes to the OSPF process on R2.
Configure a route-policy on R2 and set the cost to 200.
[R2] acl 2000
[R2-acl-basic-2000] rule permit source 192.168.10.0 0.0.0.255
[R2-acl-basic-2000] quit
[R2] route-policy static2ospf permit node 10
[R2-route-policy] if-match acl 2000
[R2-route-policy] apply cost 200
[R2-route-policy] quit
[R2] route-policy static2ospf permit node 20
[R2-route-policy] quit
[R2] ospf
[R2-ospf-1] import-route static route-policy static2ospf type 2
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S4
Core-2
S2
Border-2
R2
OSPF
Area 2
Static routing
OSPF
Area 1
OSPF
Area 0
192.168.10.0/24
192.168.20.0/24
Imported finance department routes
Type: Type 2
Cost: 100
Imported finance department routes
Type: Type 2
Cost: 200
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 41: Example for Configuring OSPF Route Control (3)
Set the OSPF cost of an interface (GE0/0/1 of R1 is used as an example).
[R1] interface GigabitEthernet 0/0/1
[R1-GigabitEthernet0/0/1] ospf cost 50
AGG-1
S3
Finance department client
Marketing department client
Core-1
S1
Border-1
R1
AGG-2
S4
Core-2
S2
Border-2
R2
OSPF
Area 2
Static routing
OSPF
Area 1
OSPF
Area 0
192.168.10.0/24
192.168.20.0/24
Cost=10
Cost=10
Cost=50
Cost=10
Cost=50
Cost=50
GE0/0/1
Overview
Equal-Cost Route
Default Route
LSA Filtering
Configuration Case
Finance server
Marketing server

## Slide 42
OSPF Fast Convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 43: OSPF Multi-Process
OSPF supports multiple processes that can separately run on the same device and do not affect each other. Route exchange between different OSPF processes is similar to route exchange between different routing protocols.
An interface on a router can belong to only one OSPF process.
Usage scenario:
  A typical application of OSPF multi-process is in the VPN scenario.
  As shown in the figure, a PE connects to two different VPN customers, and OSPF is deployed between the PE and CEs. Therefore, multiple processes can be deployed on the PE to isolate the VPN customers.
VPN1
Site1
CE1
VPN2
Site2
CE2
PE
OSPF 100 VPN1
Area0
Area0
OSPF 200 VPN2
[PE] ospf 100 vpn-instance VPN1
[PE-ospf-100] quit
[PE] ospf 200 vpn-instance VPN2
[PE-ospf-200] quit
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: VPN: virtual private network
If a VPN instance is specified for an OSPF process that is to be created, the OSPF process belongs to this instance. Otherwise, the OSPF process belongs to the global instance.

## Slide 44: Association Between OSPF and BGP (1)
When a new device is added or a device is restarted, network traffic may be lost during BGP convergence. This is because IGP route convergence is faster than BGP route convergence.
OSPF runs on R1, R2, R3, and R4 and full-mesh IBGP connections are established. R3 is the backup device of R2.
When the network is stable, the traffic from R1 to 10.1.5.5/32 passes through the path R1 -> R2 -> R4 -> R5.
If R2 fails, traffic is switched to the path R1 -> R3 -> R4 -> R5.
After R2 recovers, OSPF converges first because IGP route convergence is faster than BGP route convergence. If R1 needs to access 10.1.5.5/32, it searches for a BGP route with the next hop being R5. R2 then searches for the IGP route and sends traffic to R2 over the route.
After receiving the traffic, R2 searches for the BGP route. Because BGP route convergence is not complete, R2 does not find a route to 10.1.5.5/32 and therefore does not forward traffic. As a result, traffic is lost.
AS 100
R1
R3
R4
R2
10.1.5.5/32
IBGP
EBGP
AS 101
R5
1
2
3
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 45: Association Between OSPF and BGP (2)
AS 100
R1
R3
R4
R2
10.1.5.5/32
IBGP
EBGP
AS 101
R5
OSPF-BGP synchronization can be enabled to prevent traffic loss.
After OSPF-BGP synchronization is enabled on a device, the device remains as a stub router within the set synchronization period. That is, the link metric in the LSA advertised by the device is the maximum value 65535. Therefore, the device instructs other OSPF devices not to use it for data forwarding.
Enable BGP association on R2. In this way, R1 continues to forward traffic through R3, but does not forward traffic to R2 until BGP route convergence on R2 is complete.
Configure the stub router.
Configure it as a stub router.
Configuring a stub router is a special route selection method. The path with a stub router configured is not preferred.
The implementation is to set the metric to the maximum value (65535) to prevent data from being forwarded through the router. It is used to protect the link of the router and is usually used in maintenance scenarios, such as upgrade.
[Huawei-ospf-1] stub-router [ on-startup [ interval ] ]
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: Command: [Huawei-ospf-1] stub-router [ on-startup [ interval ] ]
  on-startup [ interval ]: specifies the interval for a device to remain as a stub router when the device restarts or fails. The value is an integer ranging from 5 to 65535, in seconds. The default value is 500s.
    If on-startup is not configured, the device is always a stub router. That is, the cost of all routes sent by this device is 65535.
    If on-startup is specified, the device remains as a stub router only when it restarts or fails. The duration is determined by interval. If interval is not specified, the default value of 500s is used.

## Slide 46: OSPF Forwarding Address
Forwarding address (FA):
  The FA is the address to which a data packet is forwarded before the packet reaches the advertised destination address. If the forwarding address is 0.0.0.0, the packet is forwarded to the originating ASBR.
  Type 5 AS-External LSAs and Type 7 NSSA LSAs:
OSPF Type 5 and Type 7 LSAs contain a special FA field. The introduction of FA enables OSPF to avoid the sub-optimal path problem in some special scenarios.
Network Mask |  | 
E | 0 | Metric
Forwarding Address |  | 
External Route Tag |  | 
…… |  | 
LS Age | Options | LS Type
Link State ID |  | 
Advertising Router |  | 
LS Sequence Number |  | 
LS Checksum | Length | 
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 47: Problem Occurring When No FA Is Used
OSPF runs on R2, R3, and R4 that are deployed in Area 0. OSPF is enabled on GE0/0/1 of R2 and GE0/0/1 of R3, and OSPF adjacencies are established between the two routers. However, no OSPF adjacencies are established between R1 and the two routers.
  Configure a static route destined for 10.1.1.1/32 on R2, with 10.1.123.1 as the next hop.
  R2 imports the static route to OSPF and generates a Type 5 LSA to be flooded in the area.
  After R3 receives the Type 5 LSA from R2, it calculates an external route to 10.1.1.1/32 and sets the next-hop address of the route to R2 (10.1.123.2).
The path from a router (for example, R4) in the OSPF domain to 10.1.1.1/32 is R4 -> R3 -> R2 -> R1, which is the sub-optimal path.
10.1.1.1/32
R1
R2
R3
R4
GE0/0/1
10.1.123.1
10.1.123.2
GE0/0/1
10.1.123.3
GE0/0/1
Static route to 10.1.1.1/32
The next hop is 10.1.123.1.
Type 5 LSA
10.1.1.1/32
OSPF
Imports the route to OSPF.
1
2
3
Type 5 LSA
10.1.1.1/32
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 48: Using FA to Solve the Suboptimal Path Problem
When advertising an external route destined for 10.1.1.1/32 in the OSPF area, R2 sets the FA of the corresponding Type 5 LSA to 10.1.123.1, which is the next hop of the external route.
When R3 receives the LSA, it calculates the route to 10.1.1.1/32 and finds that the FA is not 0. Therefore, R3 considers that the next hop to 10.1.1.1/32 is the address specified by the FA, that is, 10.1.123.1.
10.1.1.1/32
R1
R2
R3
R4
GE0/0/1
10.1.123.1
10.1.123.2
GE0/0/1
10.1.123.3
GE0/0/1
Static route to 10.1.1.1/32
The next hop is 10.1.123.1.
Type 5 LSA
10.1.1.1/32
FA=10.1.123.1
OSPF
Imports the route to OSPF.
1
2
3
Type 5 LSA
10.1.1.1/32
FA=10.1.123.1
Data packets sent to 10.1.1.1/32
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 49: FA Values
When an ASBR imports external routes, if the FA field in the Type 5 LSA is 0, the router considers that the data packets destined for the destination network segment should be sent to the ASBR. If the FA field in a Type 5 LSA is not 0, the router considers that the data packet destined for the destination network segment should be sent to the device identified by the FA.
The FA field can be set to a non-zero value only when all the following conditions are met:
  The ASBR activates OSPF on the interface (outbound interface of the external route) connected to the external network.
  The preceding interface is not configured as a silent interface.
  The OSPF network type of such an interface is broadcast or NBMA.
  The IP address of the interface is within the network segment specified by the network command in the OSPF configuration.
  The route to the FA must be an OSPF intra-area route or an inter-area route. In this manner, the router that receives the external LSA can add the LSA into the routing table. The next hop of the route generated using the loaded external LSA is the same as the next hop to the FA.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: Type 7 LSAs in an NSSA are translated into Type 5 LSAs.
  To advertise external routes imported by an NSSA to other areas, Type 7 LSAs must be translated into Type 5 LSAs. By default, the translator is the ABR with the largest router ID in an NSSA.
  The propagate bit (P-bit) in the Options field of an LSA header is used to notify a translator whether the Type 7 LSA needs to be translated into a Type 5 LSA. A Type 7 LSA can be translated into a Type 5 LSA only when the P-bit is set to 1 and the FA is not 0.
  The P-bit is not set for Type 7 LSAs generated by an ABR.
Note: All OSPF LSAs have the same LSA header, and the P-bit is in the Options field of the LSA header.

## Slide 50: Case: Typical FA Application in NSSA Scenarios
When multiple ABRs exist in an NSSA, the system automatically selects an ABR as a translator to translate Type 7 LSAs into Type 5 LSAs. Other ABRs do not perform LSA translation.
As shown in the figure, if the FA is not considered, R1 considers that the packet must pass through the ABR (R3) to reach the destination because the router ID of R3 is greater than that of R2. In this way, traffic is diverted to the low-bandwidth link R1 -> R3 -> R4 -> R5.
R1
Router ID 10.1.3.3
R3
R2
Router ID 10.1.2.2
R4
R5
10.1.45.5
Type 7 LSA
10.1.5.0/24
FA=10.1.45.5
Type 5 LSA
10.1.5.0/24
FA=10.1.45.5
Low-bandwidth
link
Low-bandwidth
link
High-bandwidth
link
High-bandwidth
link
Data sent to 10.1.5.0/24
Route transfer
10.1.5.0/24
Type 7 to Type 5
After the FA is introduced, traffic is transmitted to the destination network segment through a high-bandwidth link.
NSSA
Area 0
Import direct external routes.
Path without the FA used
Path with the FA used
Type7 LSA
10.1.5.0/24
FA=10.1.45.5
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: As shown in the figure:
  Configure R5 to import direct external routes and set the IP address of the FA to 10.1.45.5, which is used by R5 to access the destination network segment 10.1.5.0/24.
  R3 translates Type 7 LSAs into Type 5 LSAs and the LSAs continue to carry the FA 10.1.45.5.
  Upon receipt, R1 searches its OSPF routing table for a route to the FA and uses the next hop address of the route as the next hop address of the external route.
  Therefore, R1 will finally access the destination network segment 10.1.5.0/24 through the path R1 -> R2 -> R4 -> R5.

## Slide 51: OSPF GR
During a device restart, GR ensures uninterrupted data forwarding in the forwarding plane and prevents actions such as neighbor relationship reestablishment and route calculation in the control plane from affecting functions in the forwarding plane. This prevents service interruption caused by route flapping, ensures the data forwarding of key services, and improves the reliability of the entire network.
LS Age |  | Options | LS Type=9
Opaque Type=3 | 0 |  | 
Advertising Router |  |  | 
LS Sequence Number |  |  | 
LS Checksum |  | Length | 
TLVs (Type-Length-Value) |  |  | 
Type 9 Opaque LSAs (Grace-LSAs) are added.
OSPF implements GR through Grace-LSAs.
Such LSAs are used to inform neighbors of information such as the GR time, reason, and interface address when the GR starts and exits.
TLV types:
  Grace Period TLV: This TLV indicates the maximum hold time for a neighbor to remain in the GR Helper state. The Type value of the TLV is 1, and the length is 4 bytes. If the GR Restarter has not completed the GR process when the timer expires, the neighbor no longer functions as a GR Helper. (Mandatory)
  Graceful Restart Reason TLV: This TLV notifies a neighbor of the GR Restarter's restart reason. The Type value of the TLV is 2, and the length is 1 byte. (Mandatory)
    The value 0 indicates that the reason is unknown.
    The value 1 indicates that the software is restarted.
    The value 2 indicates that the software is reloaded or upgraded.
    The value 3 indicates that the GR Restarter performs an active/standby switchover.
  IP Interface Address TLV: This TLV is used to notify the IP address of the interface that sends Grace-LSAs. The IP address uniquely identifies a restarted device on the network. The Type value of the TLV is 3, and the length is 4 bytes.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: GR is a fault-tolerant redundancy technique and has been widely used to ensure non-stop forwarding of key services during an active/standby switchover or system upgrade.
GR reasons:
  Unknown: GR is triggered for an unknown reason.
  Software restart: GR is triggered by a command.
  Software reload/upgrade: GR is triggered by a software reloading or upgrade.
  Switch to redundant control processor: GR is triggered by an unexpected active/standby switchover.
GR classification:
  Totally GR: When a neighbor of a router does not support GR, the router exits the GR state.
  Partial GR: When a neighbor does not support GR, only the interface associated with this neighbor exits GR, whereas the other interfaces perform GR processing normally.
  Planned GR: Triggered by a command, a device is restarted or performs an active/standby switchover. Before the device restarts or performs an active/standby switchover, the Restarter sends Grace-LSAs.
  Unplanned GR: Different from the implementation of a planned GR, the implementation of an unplanned GR is as follows: A router restarts or performs an active/standby switchover due to a fault or other reasons, without sending Grace-LSAs first, and enters GR after the original standby main control board goes up. The following procedure is the same as that in a planned GR.

## Slide 52: OSPF GR Process
GR process:
GR Restarter
GR Helper
R1
R2
GR Session
Grace-LSA
LSAck
Grace-LSA
Hello packets are exchanged for neighbor negotiation, and DD packets are exchanged for LSDB synchronization.
Grace-LSAs
Flush Grace-LSAs
Before an active/standby switchover
LSAcks are sent to acknowledge received LSAs.
Active/standby switchover
End of the active/standby switchover
The original standby main control board goes up.
Enter GR
After other Grace LSAs are received, only the GR period is updated.
Adjacency: Full
GR exits normally, routes are calculated, and LSAs are generated.
Helper exits normally, and Router-LSAs are generated.
Enter Helper
Helps the Restarter complete LSDB synchronization.
Concepts related to GR
GR Restarter: indicates a device that performs a protocol restart triggered by the administrator or a fault. A GR Restarter must support GR. A device can be configured to support totally GR or partial GR.
GR Helper: indicates a neighbor of the GR Restarter. A GR Helper helps the GR Restarter maintain a stable routing relationship. Therefore, the GR Helper must support GR. The Helper can be configured to support planned GR or unplanned GR or selectively support GR through policies.
GR session: indicates a session, through which a GR Restarter and a GR Helper learn each other's GR capabilities and negotiate GR capabilities. A GR session involves implementations such as protocol restart notification and information exchanges during a protocol restart.
GR duration: The maximum GR duration is 1800s. A device can exit GR regardless of whether GR succeeds or fails, without waiting for GR to expire.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: On the Restarter:
  In planned GR mode, after a command is run to trigger an active/standby switchover on the Restarter, the Restarter sends a Grace-LSA to each neighbor to notify them of the GR period and reason, and then performs an active/standby switchover. This prevents an interruption of the neighbor relationships due to the long time taken for the original standby main control board to go up, which would otherwise cause a GR failure.
  After the original standby main control board goes up, the router notifies the routing management (RM) module that the GR starts. After the interfaces previously enabled with OSPF on the original standby main control board recover, a Grace-LSA is sent immediately to notify neighbors that the local device has started a GR. Then, another five Grace-LSAs are sent consecutively to each neighbor to ensure reception. This implementation is defined by vendors, but not in the protocol. The router does not age FIB entries in this case. Therefore, the communication is normal. If GR is not supported, the router directly ages FIB entries. As a result, routing is interrupted. In this case, the router restarts normally (non-GR process). The Grace-LSAs sent by the Restarter are used to notify neighbors that the Restarter enters GR. During GR, the neighbors retain neighbor relationships with the Restarter so that other routers are unaware of the switchover on the Restarter.
  The Restarter negotiates with its neighbors to enter the standard adjacency establishment process. The neighbor states change as follows: Down → Init → Exstart. Then, DD packets are exchanged to complete LSDB synchronization. During the update of LSAs, if the LSAs (Type 1 LSAs and Type 2 LSAs) received from a Helper do not contain the link to the local device, it indicates that the network topology has changed or the neighbor does not support the Helper mode. In this case, GR fails, and the local router exits GR and restarts normally.

## Slide 53
Notes:   Each time the neighbor relationship between the router and a neighbor enters the Full state, the router calculates routes and updates its routing table. The router, however, does not update FIB entries immediately.
  If the GR timer expires, GR fails, and the router exits GR and restarts normally.
  The router checks whether the neighbor relationships with all its neighbors reach the Full state. If so, the router floods all Grace-LSAs (with the LSA age being 3600s).
  GR exits normally. The router regenerates Router-LSAs and sends them to all the areas to which the router belongs. If some interfaces are DRs, the router regenerates Network-LSAs on the corresponding network segments. The router then recalculates routes and updates its routing table. The router updates its FIB and deletes invalid routing entries.
On the Helper:
  After receiving a Grace-LSA from the Restarter, the device enters the Helper mode if the LSAs exchanged between the two ends have no change and the received Grace-LSA matches a filtering policy. If the network topology changes, the received Grace-LSA is aged, or the device is in the Restarter state, the device cannot enter the Helper mode.
  The Helper continues to send Hello packets to the Restarter to keep the state of the adjacency between them unchanged. At this time, the Restarter's neighbor state is Exstart, and therefore the Restarter implements LSDB synchronization with the Helper. After receiving a DD packet from the Restarter, the Helper generates a SeqMismatch event. This is because the Helper is not expected to receive any DD packet when the neighbor state is Full. When the neighbor state of the Helper changes from Full to Exstart, the Helper starts to exchange DD packets with the other end to synchronize LSDBs. The DD packet sent by the Restarter does not carry complete LSAs, whereas the Helper has complete LSAs. Therefore, the neighbor state of the Helper quickly changes from Exstart to Exchange and then to Full. The Helper sends its LSAs to the Restarter for synchronization. If the Helper continues to receive Grace-LSAs with different GR periods, it updates only the GR period.
  If the GR timer expires, the GR Helper exits the Helper mode.
  When the Helper receives flooded Grace-LSAs, it indicates that the GR is complete. In this case, the Helper exits the Helper state.
  The Helper regenerates a Router-LSA on the network segment connected to the Restarter. If the Helper is a DR, it generates a Network-LSA.

## Slide 54: OSPF GR Exit
Reasons why a device exits GR:
GR Execution Result | GR Restarter | GR Helper
GR succeeds. | Before GR expires, the Restarter re-establishes neighbor relationships with all its pre-active/standby switchover neighbors. | When the GR Helper receives the Grace-LSA with the age being 3600s from the Restarter, the neighbor relationship with the Restarter is Full.
GR fails. | GR expires, and neighbor relationships have not recovered completely. The Router-LSA or Network-LSA sent by the Helper causes a failure in the bidirectional check on the Restarter. The status of the GR Restarter's interface changes. The Restarter receives a Grace-LSA generated by another router on the same network segment. Only one router can perform a GR on the same network segment at the same time. The topology of neighbors on the same network segment with the Restarter changes. | The GR Helper has not received any Grace-LSA from the Restarter when the neighbor relationship expires. The status of the Helper's interface changes. The GR Helper receives LSAs, which are different from the LSAs in its own LSDB, from other routers. You can configure the GR Helper not to perform a strict LSA check to avoid this issue. On the same network segment, the GR Helper receives Grace-LSAs from two routers at the same time. The neighbor relationships between the GR Helper and other routers change.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 55: Configuring OSPF GR (1)
[Huawei-ospf-1] opaque-capability enable
Enable the opaque LSA capability.
This command enables the opaque LSA capability so that the OSPF process can generate opaque LSAs and receive opaque LSAs from neighbors. To use the OSPF GR function, which is implemented through Type 9 LSAs, the opaque LSA capability must be enabled first.
[Huawei-ospf-1] graceful-restart [ period period | planned-only | partial ]
Enable OSPF GR and configure GR session parameters on the Restarter.
period period: specifies a GR period. The value is an integer ranging from 1 to 1800, in seconds. The default value is 120.
planned-only: indicates that the router supports only planned GR. By default, a router supports both planned GR and unplanned GR.
partial: indicates that the router supports partial GR. By default, a router supports totally GR.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: Before configuring OSPF GR, complete the following tasks:
  Configure an IP address for each involved interface to ensure that neighboring devices can communicate with each other at the network layer.
  Configure basic OSPF functions.

## Slide 56: Configuring OSPF GR (2)
[Huawei-ospf-1] graceful-restart [ period period | partial | planned-only ] * helper-role { { [ ip-prefix ip-prefix-name | acl-number acl-number | acl-name acl-name ] | ignore-external-lsa | planned-only } * | never }
(Optional) Configure the GR Helper mode and set GR session parameters on the Helper.
period period: specifies a GR period. The value is an integer ranging from 1 to 1800, in seconds. The default value is 120.
planned-only: indicates that the device supports only planned GR. By default, a device supports both planned GR and unplanned GR.
partial: indicates that the device supports partial GR. By default, the device supports totally GR.
ip-prefix ip-prefix-name: specifies the name of an IP prefix list.
acl-number acl-number: specifies the number of a basic ACL. An ACL can be used to configure a filtering policy, and the device enters the Helper mode only after received packets match the filtering policy.
acl-name acl-name: specifies the name of an ACL.
ignore-external-lsa: configures the Helper not to check Type 5 LSAs or Type 7 LSAs. By default, a Helper checks external LSAs.
never: indicates that the device does not support the Helper mode.
[Huawei] display ospf [ process-id ] graceful-restart [ verbose ]
Check OSPF GR configurations and OSPF GR information.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 57: Example for Configuring OSPF GR (1)
Routers R1, R2, and R3 each are equipped with two main control boards, which back up each other. The routers interwork through OSPF and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an OSPF process or performs an active/standby switchover in GR mode.
OSPF area 0
R1
10.1.13.0/30
R3
GE0/0/0
R2
1. Assign an IP address to each involved interface and configure OSPF on each device. The configuration details are omitted.
[R1] ospf 1
[R1-ospf-1] opaque-capability enable
[R1-ospf-1] graceful-restart
2. Enable OSPF GR on R1, R2, and R3.
.1
.3
10.1.12.0/30
GE0/0/1
.1
.2
OSPF area 1
[R2] ospf 1
[R2-ospf-1] opaque-capability enable
[R2-ospf-1] graceful-restart
[R3] ospf 1
[R3-ospf-1] opaque-capability enable
[R3-ospf-1] graceful-restart
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 58: Example for Configuring OSPF GR (2)
Routers R1, R2, and R3 each are equipped with two main control boards, which back up each other. The routers interwork through OSPF and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an OSPF process or performs an active/standby switchover in GR mode.
OSPF area 0
R1
10.1.13.0/30
R3
GE0/0/0
R2
3. Check the OSPF GR status on each router. The following example uses the command output on R1.
.1
.3
10.1.12.0/30
GE0/0/1
.1
.2
OSPF area 1
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
<R1> display ospf 1 graceful-restart
OSPF Process 1 with Router ID 10.1.13.1
Graceful-restart capability : enabled
Graceful-restart support : planned and un-planned, totally
Helper-policy support : planned and un-planned, strict lsa check
Current GR state : normal
Graceful-restart period : 120 seconds
Number of neighbors under helper:
Normal neighbors : 0
Virtual neighbors : 0
Sham-link neighbors : 0
Total neighbors : 0
Number of restarting neighbors : 0
Last exit reason:
On graceful restart : none
On Helper : none

## Slide 59: Example for Configuring OSPF GR (3)
Routers R1, R2, and R3 each are equipped with two main control boards, which back up each other. The routers interwork through OSPF and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an OSPF process or performs an active/standby switchover in GR mode.
OSPF area 0
R1
10.1.13.0/30
R3
GE0/0/0
R2
4. Run the reset ospf process graceful-restart command in the user view of R1 to restart OSPF process 1, and run the display ospf peer command on R2 to check the OSPF neighbor relationship with R1.
.1
.3
10.1.12.0/30
GE0/0/1
.1
.2
OSPF area 1
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
<R1> reset ospf 1 process graceful-restart
<R2> display ospf 1 peer
OSPF Process 1 with Router ID 10.1.12.2
Neighbors
Area 0.0.0.1 interface 10.1.12.2(GigabitEthernet0/0/0)'s neighbors
Router ID: 10.1.13.1 Address: 10.1.12.1 GR State: Doing GR
State: Full Mode: Nbr is Master Priority: 1
DR: 10.1.12.1 BDR: 10.1.12.2 MTU: 0
Dead timer due in 32 sec
Retrans timer interval: 5
Neighbor is up for 00:00:13
Authentication Sequence: [ 0 ]
The OSPF neighbor state on R2 is Full, indicating that the neighbor relationship between R1 and R2 is not interrupted when R1 restarts the OSPF process in GR mode.

## Slide 60: Example for Configuring OSPF GR (4)
5. Check the OSPF GR state on the routers. According to the following command outputs, R1 has exited the GR state normally, and R2 has exited from the Helper state normally.
<R1> display ospf 1 graceful-restart
OSPF Process 1 with Router ID 10.1.13.1
Graceful-restart capability : enabled
Graceful-restart support : planned and un-planned, totally
Helper-policy support : planned and un-planned, strict lsa check
Current GR state : normal
Graceful-restart period : 120 seconds
Number of neighbors under helper:
Normal neighbors : 0
Virtual neighbors : 0
Sham-link neighbors : 0
Total neighbors : 0
Number of restarting neighbors : 0
Last exit reason:
On graceful restart : successful exit
On Helper : none
<R2> display ospf 1 graceful-restart
OSPF Process 1 with Router ID 10.1.12.2
Graceful-restart capability : enabled
Graceful-restart support : planned and un-planned, totally
Helper-policy support : planned and un-planned, strict lsa check
Current GR state : normal
Graceful-restart period : 120 seconds
Number of neighbors under helper:
Normal neighbors : 0
Virtual neighbors : 0
Sham-link neighbors : 0
Total neighbors : 0
Number of restarting neighbors : 0
Last exit reason:
On graceful restart : none
On Helper : successful exit
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 61: NSR
High-reliability solutions include non-stop forwarding (NSF) and non-stop routing (NSR).
NSF
The GR mechanism ensures that service forwarding is not interrupted during an active/standby switchover.
If a fault occurs in the system, services in the forwarding plane are not interrupted during a system restart.
After the system recovers, it re-establishes neighbor relationships, obtains routing information from neighbors, and rebuilds its routing table.
NSR
The protocol backup mechanism ensures that routing in the control plane and services in the forwarding plane are not interrupted during an active main board (AMB)/standby main board (SMB) switchover.
Routing is not interrupted during the AMB/SMB switchover because:
Neighbor and topology information is not lost.
Neighbor relationships are not interrupted.
Advantages:
This solution does not depend on or affect the peer device. Therefore, there is no interworking problem.
Route convergence in NSR is faster than that in NSF.
NSR is a reliability technology used on a device with an AMB and SMB. It ensures that neighbor relationships are not affected when the AMB fails.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: NSR and GR:
  The system in which an AMB/SMB switchover is performed supports two types of high-reliability protection: NSR and GR.
  NSR and GR, however, are mutually exclusive. That is, for a specific protocol, only one of them can be used after a switchover.
  When NSR is deployed on a device, the device can still function as a GR Helper to support the GR process of its neighbor, ensuring high reliability of services on all nodes on the network to the greatest extent.
Application scenario:
  NSF can be used if a network has low requirements for the packet loss rate and route convergence.
  NSR can be used if a network has high requirements for the packet loss rate and route convergence.
System-level NSR is triggered in the following situations:
  A system fault triggers an AMB/SMB switchover.
  The network administrator manually triggers an AMB/SMB switchover during a software upgrade or maintenance.
Note: NSR fundamentals are the same in OSPF, IS-IS, and BGP. This course uses OSPF as an example.

## Slide 62: NSR Fundamentals
NSR is implemented in three phases:
  Batch backup: After NSR is enabled and the SMB restarts, the AMB sends routing and forwarding information in batches to the SMB for backup. Batch backup is performed before real-time backup. An AMB/SMB switchover cannot be performed during batch backup in NSR.
  Real-time backup: Real-time backup starts after batch backup is complete. All updates in the control and forwarding planes are backed up from the AMB to the SMB in real time. In this phase, the SMB can take over services from the AMB at any time.
  AMB/SMB switchover: If the AMB fails in the NSR system in which backup has been completed, the SMB detects the failure through hardware status detection and becomes the new AMB. The new AMB instructs LPUs to send packets to itself. The AMB/SMB switchover is completed rapidly, with routing between the local node and its neighbor nodes uninterrupted.
Neighbor node
AMB
SMB
LPU
Packet sending
AMB
SMB
LPU
Packet sending
NSR switchover
Neighbor node
1
2
The routing protocols in the control plane back up routing information in real time.
1
The hardware channel detects the exception on the AMB, the SMB is instructed to become the new AMB, and LPUs are instructed to send packets to the new AMB.
2
Multi-Process
Association with BGP
Forwarding Address
GR
NSR
Notes: High availability (HA): implements data backup from the AMB to the SMB.
AMB and SMB: implement control plane processes.
Line processing unit (LPU): implements forwarding plane processes.

## Slide 63: NSR Switchover Phase: Batch Backup
After NSR is enabled and the SMB restarts, the service process on the AMB receives a message indicating that the SMB goes online. Service processes then start to back up internal data in batches.
  After batch backup is complete, the device enters the redundancy protection state. If the AMB fails in this case, the SMB becomes the new AMB based on the data backed up from the original AMB and restores services.
  If the AMB fails before batch backup is complete, the SMB may fail to become the new AMB due to incomplete service data. As a result, an NSR switchover cannot be performed; in this case, the device restarts and restores the pre-fault status.
AMB
SMB
LPU
Packet sending
OSPF
BGP
APPCFG
Packet
OSPF
BGP
APPCFG
Packet
1
2
3
The SMB completes startup.
Service processes start backing up service data such as routes in batches through the HA channel. The system enters the batch backup phase.
After service processes complete batch backup, the system enters the redundancy protection state.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 64: NSR Switchover Phase: Real-Time Backup
After batch backup is complete, the device enters the real-time backup phase. If the neighbor status or routing information changes in this phase, the AMB backs up the updated information to the SMB in real time.
AMB
SMB
LPU
Packet sending
OSPF
BGP
Packet
OSPF
BGP
Packet
2
3
1
1
The neighbor status or routing information changes.
The AMB backs up updated information to the SMB through the HA channel.
The SMB sends an acknowledgement to the AMB.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 65: NSR Switchover Phase: AMB/SMB Switchover
After the batch backup is complete, the system enters the redundancy protection state. If a software or hardware fault occurs on the AMB, the SMB detects the fault on the AMB through underlying hardware detection and automatically becomes the new AMB.
The new AMB uses the data backed up from the original AMB to process services. At the same time, LPUs send the information updated during the switchover to the new AMB. Routing and traffic forwarding are not interrupted in this case.
AMB
SMB
LPU
Packet sending
OSPF
BGP
IFNET
Forwarding Plane
OSPF
BGP
1
2
3
AMB
OSPF
BGP
Forwarding Plane
Forwarding Plane
IFNET
IFNET
The hardware channel detects the exception on the AMB, the SMB is instructed to become the new AMB, and LPUs are instructed to send packets to the new AMB.
After the original SMB becomes the new AMB, LPUs send the information updated during the switchover to the new AMB.
IFNET
Forwarding Plane
After the switchover is complete, the new AMB performs NSR backup to the new SMB.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 66: Configuring NSR
[Huawei] switchover mode { nonstop-routing | nonstop-forwarding }
Enable NSR.
This command is used to set an HA working mode. The default HA working mode is NSF.
nonstop-routing: sets the HA working mode to NSR. In NSR mode, the system can process routes and forward services without interruption.
nonstop-forwarding: sets the HA working mode to NSF. The NSF mode greatly reduces the service interruption time.
[Huawei] display switchover mode
Verify the configuration.
Check the HA working mode of the current system.
[Huawei] display ip routing-table [ vpn-instance vpn-instance-name ] [ verbose ]
Check post-AMB/SMB switchover routing information.
[Huawei] display fib [ slot-id ] [ vpn-instance vpn-instance-name ] [ verbose ]
Check post-AMB/SMB switchover forwarding information.
Multi-Process
Association with BGP
Forwarding Address
GR
NSR

## Slide 67
OSPF Fast Convergence
OSPF Route Control
Other OSPF Features
Advanced IS-IS Features

## Slide 68: Overview of IS-IS Fast Convergence
IS-IS fast convergence is an extended feature designed to speed up route convergence. It provides a series of functions, covering incremental SPF (I-SPF), PRC, intelligent timer, and LSP fast flooding.
IS-IS supports fast convergence after a fault is rectified. For example, IS-IS auto FRR can be used to quickly switch traffic to a backup link, and IS-IS can be associated with BFD to quickly detect faults.
Fast Convergence
Routing Control
Other Features
Notes: The functions, including PRC, intelligent timer, and FRR of IS-IS are similar to those of OSPF and therefore not detailed here.

## Slide 69: I-SPF
I-SPF implementation: When the network topology changes, I-SPF recalculates routes only for affected nodes instead of all nodes, speeding up route calculation.
In route calculation, a node represents a router, and a leaf represents a route. I-SPF processes the information of only changed nodes.
Scenario description:
  On an IS-IS network, an SPT with R1 as the root is calculated after route convergence, as shown in the left figure. When R1 accesses R5, the traffic of R1 is forwarded to R5 based on [the outbound interface of R1's downlink and the IP address of the inbound interface of R3's uplink].
  R6 is added as a downstream device of R5. IS-IS is enabled on R6, meaning that there is a new network node on the IS-IS network.
I-SPF calculation:
  R5 and R6 both flood LSPs carrying information about their neighbor relationship on the entire network.
  After receiving such an LSP, R1 performs I-SPF calculation only for R5 and R6 to generate a new SPT.
  Therefore, when R1 accesses R5 and R6, the traffic of R1 is forwarded to R5 and R6 based on [the outbound interface of R1's downlink and the IP address of the inbound interface of R3's uplink].
R1 (root)
R2
R3
R4
R5
R6 (new)
Fast Convergence
Routing Control
Other Features
Notes: SPF for route calculation: If a node on a network changes, SPF recalculates routes for all the nodes on the network, which takes a long time, consumes a large number of CPU resources, and consequently reduces the network-wide convergence speed.
I-SPF is an improvement of SPF. Unlike SPF that calculates all nodes, I-SPF calculates only affected nodes. The SPT generated using I-SPF is the same as that generated using SPF. This significantly decreases CPU usage and speeds up network convergence.
I-SPF and PRC are used together on an IS-IS network.
  If the SPT calculated by I-SPF changes, PRC processes all the leaves (routes) of only the changed node.
  If the SPT calculated by I-SPF does not change, PRC processes only the changed leaves (routes). For example, if IS-IS is newly enabled on an interface of a node, the SPT on the network remains unchanged. In this case, PRC updates only the routes of this interface, which consumes less CPU resources.

## Slide 70: LSP Fast Flooding
LSP fast flooding: speeds up the flooding of LSPs.
  Generally, when an IS-IS router receives new or updated LSPs from other routers, it updates the local LSDB and periodically floods the involved LSPs.
  LSP fast flooding speeds up LSDB synchronization because it allows a device to flood a number of LSPs (not exceeding the upper limit) before route calculation when the device receives one or more new or updated LSPs. This flooding mode significantly speeds up the network-wide convergence speed.
  Enable LSP fast flooding.
Note: You can specify the maximum number of LSPs to be flooded at a time. Once specified, the number takes effect on all IS-IS interfaces. The actual number of LSPs that can be sent at a time is limited to the number specified by lsp-count.
[Huawei-isis-1] flash-flood [ lsp-count | max-timer-interval interval | [ level-1 | level-2 ] ]
Fast Convergence
Routing Control
Other Features
Notes: Command: [Huawei-isis-1] flash-flood [ lsp-count | max-timer-interval interval | [ level-1 | level-2 ] ]
  lsp-count: specifies the maximum number of LSPs that can be flooded on each interface at a time. The value is an integer ranging from 1 to 15. The default value is 5.
  max-timer-interval interval: specifies the maximum interval at which LSPs are flooded. The value is an integer ranging from 10 to 50000, in milliseconds. The default value is 10.
  level-1: enables the LSP flash-flood function in the Level-1 area. If no level is specified in the command, this function is enabled in both Level-1 and Level-2 areas.
  level-2: enables the LSP flash-flood function in the Level-2 area. If no level is specified in the command, this function is enabled in both Level-1 and Level-2 areas.

## Slide 71: Overview of IS-IS Route Control
In real-world applications, IS-IS routes calculated using SPF sometimes cannot meet network planning and traffic management requirements, which may lead to various problems, such as slow table lookup due to a large number of routing entries in routing tables and unbalanced link usage on a network. To optimize IS-IS networks and facilitate traffic management, more precise route control is required. You can use any of the following methods to implement the control:
  Adjusting the IS-IS preference
  Adjusting the IS-IS interface cost
  Configuring equal-cost routes
  Configuring IS-IS route leaking
  Configuring default route advertisement
  Importing external routes
  Configuring filter-policies
Fast Convergence
Routing Control
Other Features
Notes: This course involves only equal-cost and default routes. For details about other control methods, see HCIP-Datacom-Core Technology.

## Slide 72: Equal-Cost Route
If there are multiple redundant links on an IS-IS network, multiple equal-cost routes to the same destination may exist. In this case, you can use either of the following methods to configure equal-cost routes:
  Configure load balancing so that traffic is evenly distributed to relevant links.
    This method improves link utilization and reduces the possibility of congestion caused by overloaded links. However, because traffic will be randomly forwarded, this method may make traffic management difficult.
  Configure a preference for each equal-cost route so that the route with the highest preference is preferentially selected and the others function as backups.
    This method is used to specify the preferred route among multiple equal-cost routes, without the need to modify original configurations. It facilitates traffic management and improves network reliability.
    Note: After preferences are configured for equal-cost routes, IS-IS devices forward traffic to the next hop with the highest preference, instead of forwarding traffic in load balancing mode.
Fast Convergence
Routing Control
Other Features

## Slide 73: Configuration of Equal-Cost IS-IS Routes
If the number of equal-cost routes is greater than the number specified using the maximum load-balancing command, routes are selected for load balancing according to the following rules in sequence:
  Route preference: Routes with smaller preference values (higher preferences) are selected for load balancing.
  Next-hop system ID: If all equal-cost routes have the same preference, routes with smaller next-hop system IDs are selected for load balancing.
  Local outbound interface index: If all equal-cost routes have the same preference and next-hop system ID, routes with smaller local outbound interface indexes are selected for load balancing.
Configure load balancing among equal-cost IS-IS routes.
Configure the maximum number of equal-cost routes that participate in load balancing.
Configure preferences for equal-cost IS-IS routes.
By default, no preferences are configured for equal-cost IS-IS routes. A smaller value indicates a higher preference.
[Huawei-isis-1] maximum load-balancing number
[Huawei-isis-1] nexthop ip-address weight value
Fast Convergence
Routing Control
Other Features
Notes: Command: [Huawei-isis-1] maximum load-balancing number
  number: specifies the maximum number of equal-cost routes that participate in load balancing. The value varies according to the device model.
Command: [Huawei-isis-1] nexthop ip-address weight value
  ip-address: specifies the IP address of the next hop. The value is in dotted decimal notation.
  weight value: specifies the weight of the next hop. A smaller value indicates a higher preference. The value is an integer ranging from 1 to 254.

## Slide 74: Example for Configuring Equal-Cost Routes (1)
On the network shown in the figure, IS-IS runs on R1, R2, and R3. It is required that R1 be able to access the loopback interface address of R3 through path R1 -> R3 or R1 -> R2 -> R3.
Device | Interface | IP Address
R1 | GE0/0/0 | 10.1.13.1/24
 | GE0/0/1 | 10.1.12.1/24
R2 | GE0/0/1 | 10.1.12.2/24
 | GE0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE0/0/0 | 10.1.13.3/24
 | GE0/0/2 | 10.1.23.3/24
1. Assign IP addresses to device interfaces and configure IS-IS on each device. (Omitted)
2. Configure the number of IS-IS equal-cost routes for load balancing on R1.
3. Verify the configuration.
IS-IS
R1
Cost=10
Cost=5
Cost=5
R3
GE0/0/0
GE0/0/1
GE0/0/2
R2
[R1] isis
[R1-isis-1] maximum load-balancing 2
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 ISIS-L2 15 10 D 10.1.13.3 GigabitEthernet0/0/0
ISIS-L2 15 10 D 10.1.12.2 GigabitEthernet0/0/1
Fast Convergence
Routing Control
Other Features

## Slide 75: Example for Configuring Equal-Cost Routes (2)
On the network shown in the figure, IS-IS runs on R1, R2, and R3. It is required that R1 be able to access the loopback interface address of R3 through path R1 -> R3 or R1 -> R2 -> R3.
Device | Interface | IP Address
R1 | GE0/0/0 | 10.1.13.1/24
 | GE0/0/1 | 10.1.12.1/24
R2 | GE0/0/1 | 10.1.12.2/24
 | GE0/0/2 | 10.1.23.2/24
R3 | Loopback0 | 10.1.3.3/32
 | GE0/0/0 | 10.1.13.3/24
 | GE0/0/2 | 10.1.23.3/24
1. Assign IP addresses to device interfaces and configure IS-IS on each device. (Omitted)
2. (Optional) Configure preference for equal-cost routes on R1.
3. Verify the configuration.
IS-IS
R1
Cost=10
Cost=5
Cost=5
R3
GE0/0/0
GE0/0/1
GE0/0/2
R2
[R1] isis
[R1-isis-1] nexthop 10.1.13.3 weight 1
[R1-isis-1] nexthop 10.1.12.2 weight 2
[R1]display ip routing-table
Route Flags: R - relay, D - download to fib
-------------------------------------------------------------------------------------------
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.3.3/32 ISIS-L2 15 10 D 10.1.13.3 GigabitEthernet0/0/0
Fast Convergence
Routing Control
Other Features

## Slide 76: Default Route
IS-IS allows you to control the generation and advertisement of default routes using the following methods:
  On Level-1-2 devices, configure a rule for setting the attached (ATT) bit in Level-1 LSPs.
  Configure Level-1 devices not to automatically generate default routes even if they receive Level-1 LSPs with the ATT bit set to 1.
  Configure devices to advertise default routes to the IS-IS routing domain.
LSP packet format:
  The ATT bit is generated by a Level-1-2 router to identify whether the originating router connects to other areas. Note that the ATT field has four bits, and Huawei datacom products use only one of the four bits.
PDU Common Header
PDU Specific Header
Variable Length Fields（TLV）
PDU Length |  |  | 
Remaining Lifetime |  |  | 
LSP ID |  |  | 
Sequence Number |  |  | 
Checksum |  |  | 
P | ATT | OL | IS Type
Fast Convergence
Routing Control
Other Features

## Slide 77: Setting the ATT Bit to Control the Generation of Default Routes
In IS-IS, if a Level-1-2 device determines based on LSDB information that it can reach more areas through a Level-2 area than through a Level-1 area, the device sets the ATT bit to 1 in Level-1 LSPs before advertising these LSPs. Upon receipt, Level-1 devices generate default routes destined for this Level-1-2 device.
The preceding rules are applied by default. The ATT bit can be set as required on a live network.
(Level-1-2 device) Configure a rule for setting the ATT bit in LSPs.
By default, the Level-1-2 device sets the ATT bit in LSPs following the default rules.
(Level-1 device) Configure the device not to generate a default route after it receives LSPs carrying ATT bit 1.
By default, a Level-1 device generates a default route after it receives LSPs carrying ATT bit 1.
[Huawei-isis-1] attached-bit advertise { always | never }
[Huawei-isis-1] attached-bit avoid-learning
Fast Convergence
Routing Control
Other Features
Notes: Command: [Huawei-isis-1] attached-bit advertise { always | never }
  always: indicates that the ATT bit is set to 1. After receiving an LSP with ATT bit 1, a Level-1 device generates a default route.
  never: indicates that the ATT bit is set to 0. This prevents the Level-1 device from generating default routes and reduces the size of the routing table.
Although the ATT bit is defined in both Level-1 and Level-2 LSPs, it is set to 1 only in Level-1 LSPs advertised by Level-1-2 devices. Therefore, this command takes effect only on Level-1-2 devices.
To prevent Level-1 devices from advertising default routes to their routing tables, perform either of the following operations:
  Run the attached-bit advertise never command on Level-1-2 devices to disable them from advertising LSPs with ATT bit 1.
  Run the attached-bit avoid-learning command on Level-1 devices that connect to Level-1-2 devices.
The difference between the preceding commands lies in that the attached-bit avoid-learning command applies to specified Level-1 devices.

## Slide 78: Configuring Devices to Advertise Default Routes to the IS-IS Routing Domain
After the default-route-advertise command is run on a boundary device in the IS-IS domain, the device advertises default route 0.0.0.0/0 to the IS-IS routing domain. After that, all traffic destined for other routing domains is forwarded to this boundary device first, and the device then forwards the traffic outside the IS-IS routing domain.
Generally, if other routing protocols are configured in addition to IS-IS, use the following two methods to forward traffic in the IS-IS routing domain to other routing domains:
  Configure boundary devices to advertise default routes to the IS-IS routing domain. This method is simple and does not require external route learning.
  Configure boundary devices to import routes of other routing protocols into IS-IS.
Configure an IS-IS device to generate a default route.
By default, an IS-IS device does not generate the default route.
[Huawei-isis-1] default-route-advertise [ always | match default | route-policy route-policy-name ] [ cost cost | tag tag | [ level-1 | level-1-2 | level-2 ] ] [ avoid-learning ]
Fast Convergence
Routing Control
Other Features
Notes: Command: [Huawei-isis-1] default-route-advertise [ always | match default | route-policy route-policy-name ] [ cost cost | tag tag | [ level-1 | level-1-2 | level-2 ] ] [ avoid-learning ]
  always: configures an IS-IS device to unconditionally advertise the default route and set itself as the next hop in the route.
  match default: advertises the default route generated by another routing protocol or IS-IS process through LSPs if such a route already exists in the routing table.
  route-policy route-policy-name: specifies the name of the route-policy. A Level-1-2 device advertises the default route to the IS-IS routing domain only when external routes matching the route-policy exist in the routing table of the device. This prevents routing blackholes caused by the advertisement of the default route when link faults make some important external routes unavailable. This route-policy does not affect the import of external routes into IS-IS. The value is a string of 1 to 40 case-sensitive characters, spaces not supported. If spaces are used, the string must start and end with double quotation marks (").
  cost cost: specifies the cost of the default route. The value is an integer. The value range depends on cost-style. When cost-style is narrow, narrow-compatible, or compatible, the value ranges from 0 to 63. When cost-style is wide or wide-compatible, the value ranges from 0 to 4261412864.

## Slide 79
Notes:   tag tag: specifies the tag value of the default route to be advertised. The advertised LSPs carry the tag value only when the IS-IS cost type is wide, wide-compatible, or compatible. The value is an integer ranging from 1 to 4294967295.
  level-1: sets the level of the default route to be advertised to Level-1. If the level is not specified, a Level-2 default route is generated by default.
  level-2: sets the level of the default route to be advertised to Level-2. If the level is not specified, a Level-2 default route is generated by default.
  level-1-2: sets the level of the default route to be advertised to Level-1-2. If the level is not specified, a Level-2 default route is generated by default.
  avoid-learning: prevents an IS-IS process from learning default routes or adding them to the routing table. If a default route exists in the routing table and is in the active state, set the route to inactive.
After this command is run on a device, all traffic in the IS-IS routing domain will be forwarded by this device to a destination outside the domain. Compared with configuring a static default route on each router in an IS-IS routing domain, running this command simplifies configurations, because this command only needs to be run on boundary routers in the IS-IS routing domain. In addition, the default-route-advertise command enables dynamic default route advertisement, and you can specify different parameters to allow the default route to be advertised in different ways.
If this command is run on a Level-1 device, the device advertises the default route only to the Level-1 area.

## Slide 80: Example for Configuring Default Routes
As shown in the figure, OSPF runs on GE0/0/1 and Loopback0 of R1 and GE0/0/1 of R2, and IS-IS runs on GE0/0/2 of R2 and R3.
To enable R3 to access the OSPF network, configure R2 to advertise the default route to the IS-IS routing domain.
Similarly, R2 also needs to advertise the default route to the OSPF routing domain.
1. Assign an IP address to each interface and configure OSPF/IS-IS on each device.
2. Configure R2 to advertise the default route to the IS-IS routing domain.
3. Configure R2 to advertise the default route to the OSPF routing domain.
4. Check routing entries on R3.
OSPF
IS-IS
R1
R2 L2
R3 L2
GE0/0/1
GE0/0/2
10.1.12.0/24
10.1.23.0/24
Loopback0：
10.1.1.1/32
[R2] isis
[R2-isis-1] default-route-advertise always
[R2] ospf
[R2-ospf-1] default-route-advertise always
[R3]display ip routing-table
Route Flags: R - relay, D - download to fib
---------------------------------------------------------------------------------------
Routing Tables: Public
Destinations : 8 Routes : 8
Destination/Mask Proto Pre Cost Flags NextHop Interface
0.0.0.0/0 ISIS-L2 15 10 D 10.1.23.2 GigabitEthernet0/0/2
……
Fast Convergence
Routing Control
Other Features

## Slide 81: IS-IS Multi-Instance and Multi-Process
In IS-IS multi-instance, multiple IS-IS processes are created on the same router, with each process associated with one VPN instance.
In IS-IS multi-process, multiple IS-IS processes are created in the same VPN instance (or in the same public network instance). These IS-IS processes are independent of each other. IS-IS processes function similarly to different routing protocols in route exchange.
A network may carry different services, which need to be isolated for security. You can bind each IS-IS process to a different VPN instance.
Application scenarios:
  IS-IS multi-instance and multi-process are typically used in VPN scenarios.
  As the figure shown, a PE is connected to two VPNs, each belonging to a different customer, and IS-IS is deployed between the PE and CEs. You can configure multiple IS-IS processes on the PE to isolate the VPN customers.
VPN1
Site1
CE1
VPN2
Site2
CE2
PE
isis 100 VPN1
Isis 200 VPN2
[PE] isis 100 vpn-instance VPN1
[PE-isis-100] quit
[PE] isis 200 vpn-instance VPN2
[PE-isis-200] quit
Fast Convergence
Routing Control
Other Features
Notes: IS-IS multi-process and multi-instance have the following characteristics:
  In IS-IS multi-process, processes share the same global routing table. IS-IS multi-instance, however, uses the routing tables of VPNs, with each VPN having a separate routing table.
  IS-IS multi-process allows a set of interfaces to be associated with a specified IS-IS process. This ensures that the protocol operations in the specified IS-IS process are confined only to this set of interfaces. In this way, multiple IS-IS processes can work on a single router, with each process responsible for a unique set of interfaces.
  When creating an IS-IS process, you can bind it to a VPN instance. The IS-IS process then accepts and processes only the events related to the VPN instance. When the bound VPN instance is deleted, the IS-IS process is also deleted.
Command: [Huawei] isis [ process-id ] [ vpn-instance vpn-instance-name ]
  process-id: specifies the ID of an IS-IS process. If no IS-IS process is specified, IS-IS process 1 is started. The value is an integer ranging from 1 to 65535. The default value is 1.
  vpn-instance vpn-instance-name: specifies the name of a VPN instance. If this parameter is not specified, no VPN instance is associated with the IS-IS process. The value is a string of 1 to 31 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").

## Slide 82: LSP Fragment
When a PDU to be advertised by IS-IS contains too much information, an IS-IS router generates LSP fragments to carry the information.
LSP packet format
An IS-IS LSP fragment is identified by the 1-byte LSP Number field in LSP ID. So, an IS-IS process can generate a maximum of 256 LSP fragments, which means only limited information can be carried.
PDU Common Header
PDU Specific Header
Variable Length Fields（TLV）
PDU Length |  |  | 
Remaining Lifetime |  |  | 
LSP ID |  |  | 
Sequence Number |  |  | 
Checksum |  |  | 
P | ATT | OL | IS Type
System ID (6 bytes)
Pseudonode ID (1 byte)
LSP Number (1 byte)
Fast Convergence
Routing Control
Other Features

## Slide 83: Basic Concepts of LSP Fragment Extension
You can configure a virtual system ID for IS-IS to generate virtual IS-IS LSPs to carry routing information.
  Originating system: a router that actually runs IS-IS. A single IS-IS process can advertise LSPs like multiple virtual routers, and the originating system refers to the "actual" (not virtual) IS-IS process.
  Normal system ID: system ID of the originating system.
  Virtual system: system identified by an additional system ID to generate extended LSP fragments. These fragments carry additional system IDs in their LSP IDs.
  Additional system ID: system ID of a virtual system. It is assigned by a network administrator to identify a virtual system. A maximum of 256 extended LSP fragments can be generated for each additional system ID.
  TLV 24 (IS Alias ID TLV): carried in LSP fragments and describes the relationship between the originating and virtual systems.
Type=24
Length
Value： Normal System-ID
Fast Convergence
Routing Control
Other Features
Notes: After LSP fragment extension is configured, the system prompts you to restart the IS-IS process if information is lost because LSPs overflow. After the IS-IS process is restarted, the originating system loads as much routing information as possible to its LSPs. The information that cannot be loaded is placed in the LSPs of virtual systems for transmission. The originating system then notifies other routers of its relationship with the virtual systems through TLV 24.
Note: the additional and normal system IDs must be unique throughout a routing domain.

## Slide 84: Implementation of LSP Fragment Extension
In IS-IS, each normal system ID identifies a system, which can generate a maximum of 256 LSP fragments. With additional system IDs, up to 50 virtual systems can be configured, and an IS-IS process can then generate a maximum of 13,056 LSP fragments.
LSP fragment extension can work in two modes.
Mode-1
Used when some routers on the network do not support LSP fragment extension.
As the figure shown, R1 loads some routing information to the LSPs of R1-1 and R1-2 for transmission. When R2 receives the LSPs from R1, R1-1, and R1-2, it considers that there are three independent routers at the peer end and calculates routes as normal. The costs of the routes from R1 to R1-1 and from R1 to R1-2 are both 0, meaning that the routes from R2 to R1 and from R2 to R1-1/R1-2 share the same cost.
Mode-2
Used when all the routers on the network support LSP fragment extension.
As the figure shown, R1 loads some routing information to the LSPs of R1-1 and R1-2 for transmission. When R2 receives LSPs from R1-1 and R1-2, it knows that their originating system is R1 based on TLV 24. R2 then considers information advertised by R1-1 and R1-2 as information of R1.
R2
Does not support LSP fragment extension.
R1
R1-1
R1 virtual system
R1-2
R1 virtual system
LSP
LSP-1
LSP-2
R2
R1
R1-1
R1 virtual system
R1-2
R1 virtual system
LSP
LSP-1
LSP-2
Calculates routes separately for the received LSP-1 and LSP-2.
Considers received LSP-1 and LSP-2 both the routing information of R1 and calculates routes uniformly.
Fast Convergence
Routing Control
Other Features
Notes: Mode-1 implementation:
  Virtual systems participate in SPF calculation. The LSPs advertised by the originating system contain information about links to each virtual system. Similarly, the LSPs advertised by each virtual system contain information about links to the originating system. In this way, virtual systems function like physical routers that connect to the originating system.
  Mode-1 is a transitional mode used to support earlier versions that are incapable of LSP fragment extension. In these earlier versions, IS-IS cannot identify TLV 24. As a result, the LSPs sent by a virtual system must look like LSPs sent by an originating system.
  Precautions:
    The LSPs sent by a virtual system must contain the same area address and overload bit as those in LSPs sent by an originating system. Other TLVs must also be the same.
    The neighbor of a virtual system must point to an originating system, and the metric is the maximum value minus 1. The neighbor of the originating system must point to the virtual system, and the metric must be 0. This ensures that the virtual system is the downstream node of the originating system when other routers calculate routes.
Mode-2 implementation:
  Virtual systems do not participate in SPF calculation. All the routers on the network know that the LSPs generated by the virtual systems actually belong to the originating system.
  IS-IS working in mode-2 can identify TLV 24, which is used as the basis for calculating an SPT and routes.
Note: In both modes, the originating system and virtual systems must include TLV 24 in their LSPs whose LSP Number is 0 to indicate which is the originating system.

## Slide 85: Basic Configuration Commands of LSP Fragment Extension
Note: The preceding two commands must be used together. The configured virtual system ID takes effect only after LSP fragment extension is enabled and the IS-IS process is restarted using the reset isis all command.
Enable LSP fragment extension for an IS-IS process.
By default, LSP fragment extension is disabled for IS-IS processes.
If no mode or level is specified during the configuration of LSP fragment extension, mode-1 and level-1-2 are used by default.
Configure a virtual system.
By default, no virtual system is configured.
To enable a device to generate extended LSP fragments, you must configure at least one virtual system ID. This ID must be unique throughout a routing domain.
An IS-IS process can be configured with up to 50 virtual system IDs.
[Huawei-isis-1] lsp-fragments-extend [ [ level-1 | level-2 | level-1-2 ] | [ mode-1 | mode-2 ] ]
[Huawei-isis-1] virtual-system virtual-system-id
Fast Convergence
Routing Control
Other Features
Notes: Command: [Huawei-isis-1] lsp-fragments-extend [ [ level-1 | level-2 | level-1-2 ] | [ mode-1 | mode-2 ] ]
  level-1: enables LSP fragment extension in Level-1.
  level-2: enables LSP fragment extension in Level-2.
  level-1-2: enables LSP fragment extension in Level-1-2.
  mode-1: allows routers to be compatible with other routers running earlier versions that are incapable of LSP fragment extension.
  mode-2: requires all routers to support LSP fragment extension.
Command: [Huawei-isis-1] virtual-system virtual-system-id
  virtual-system-id: specifies a virtual system ID of an IS-IS process. The length is 6 bytes (48 bits), and the format is XXXX.XXXX.XXXX.

## Slide 86: IS-IS GR
IS-IS GR is a high-reliability technology that supports GR and can ensure non-stop data forwarding.
To implement GR, IS-IS uses the TLV (Restart TLV) with the Type value 211 and three timers: T1, T2, and T3.
Type = 211 |  |  | 
Length |  |  | 
Reserved | SA | RA | RR
Remaining Time |  |  | 
Restart TLV
The Restart TLV is included in the extension part of an IS-to-IS Hello (IIH) PDU. All IIH packets of a device that supports IS-IS GR contain the Restart TLV. The Restart TLV carries some parameters for the protocol restart.
Timers
T1 timer: If the GR Restarter has sent an IIH packet with RR being set but has not received any IIH packet in which the Restart TLV is carried and RA is set from the GR Helper when the T1 timer expires, the GR Restarter resets the T1 timer and continues to send IIH packets with the Restart TLV. If an acknowledgement packet is received or the T1 timer expires three times, the T1 timer is canceled. The default value of the T1 timer is 3s.
T2 timer: It indicates the period from the time when the GR Restarter restarts to the time when the LSDBs of all devices of the same level are synchronized. T2 is the maximum time that the system waits for synchronization of all LSDBs. T2 is generally 60 seconds.
T3 timer: It indicates the maximum time allowed for the GR Restarter to complete GR successfully. The initial value of the T3 timer is 65535s. If the T3 timer expires, GR fails.
SA: is short for Suppress Adjacency Advertisement.
RA: is short for Restart Acknowledgment.
RR: is short for Restart Request.
Remaining Time: indicates the remaining time before the neighbor resets the adjacency.
Fast Convergence
Routing Control
Other Features
Notes: Background:
  After an active/standby switchover is performed on a device, because the device has not stored any information about the neighbor relationships established before the restart, the initial Hello packets sent by the device carry an empty neighbor list. After receiving the Hello packets, a neighbor (Helper device) performs the two-way neighbor relationship check. After the neighbor detects that it is not in the neighbor list in the Hello packets sent by the Restarter, the neighbor tears down the neighbor relationship. The neighbor then generates new LSPs and floods the topology changes to all other devices in the area. The other devices in the area then calculate routes based on their new LSDBs, leading to routing interruptions or routing loops.
  The IETF defined the GR standard (RFC 3847) for IS-IS. The protocol restarts in which the FIB is retained and the protocol restarts in which the FIB is not retained are both processed, preventing route flapping and traffic interruptions caused by protocol restarts.

## Slide 87
Notes: TLV with Type value 211:
  Type: indicates the TLV type and is 1 byte long. Type value 211 indicates the Restart TLV.
  Length: indicates the length of the TLV value and is 1 byte long.
  SA: is used to suppress adjacency advertisement and is 1 bit long. It is used by a starting device to request its neighbors to suppress the broadcast of the neighbor relationships with the starting device to prevent routing black holes.
  RA: is used for restart acknowledgment and is 1 bit long. If a device sends to a neighbor a Hello packet in which RA is set, the packet is used to notify the neighbor that the device has received a packet in which RR is set.
  RR: indicates the restart request bit and is 1 bit long. If a device sends to a neighbor a Hello packet in which RR is set, the packet is used to notify the neighbor that the device is restarting or starting and to request the neighbor to retain the current IS-IS adjacency and respond with CSNPs.
  Remaining Time: indicates the remaining time before the neighbor resets the adjacency. The value is in seconds. This field is 2 bytes long. When RA is reset, this field is mandatory.
Supplementary description of the timers:
  T1 timer: Each interface in a process enabled with IS-IS GR maintains a T1 timer. On a Level-1-2 router, broadcast interfaces maintain a T1 timer for each level.
  T2 timer: Level-1 and Level-2 LSDBs each have a T2 timer maintained.
  T3 timer: The initial value of the T3 timer is 65535s. After the IIH packets in which RA is set are received from neighbors, the T3 value is changed to the smallest value of the Remaining Time field in the IIH packets. The entire system maintains one T3 timer.

## Slide 88: IS-IS GR Process (Restarting) (1)
The GR process triggered by an active/standby switchover or the restart of an IS-IS process is referred to as restarting, in which the FIB remains unchanged.
GR Restarter
GR Helper
R1
R2
GR Session
IIH (Restart TLV: RR=1, RA=0, SA=0)
CSNP
LSP flooding
LSPs
Active/standby switchover
Starts T1, T2, and T3 timers.
Updates the FIB.
IIH (Restart TLV: RR=0, RA=1, SA=0)
Resets the T3 timer.
Cancels the T1 timer.
Cancels the T2 timer.
Cancels the T3 timer.
Updates the FIB.
After performing a protocol restart, the GR Restarter performs the following actions:
  Starts T1, T2, and T3 timers.
  Sends IIH packets that contain the Restart TLV through all interfaces. In the packets, RR is set, and RA and SA are cleared.
After receiving an IIH packet, the GR Helper performs the following actions:
  Maintains the neighbor relationship and updates the current Holdtime.
  Replies with an IIH packet containing the Restart TLV. In the packet, RR is cleared, RA is set, and Remaining Time indicates the period from the current moment to the timeout of the Holdtime.
  Sends CSNPs and all LSPs to the GR restarter.
After receiving the IIH packet, in which RR is 0 and RA is 1, from the neighbor, the GR Restarter performs the following actions:
  Compares the current value of the T3 timer with the value of Remaining Time in the packet. The smaller value is used as the value of the T3 timer.
  Cancels the T1 timer maintained by the interface when the interface receives an acknowledgement and CSNPs.
  Resets the T1 timer and resends the IIH packet that contains the Restart TLV when the T1 timer expires but the interface has not received any acknowledgement or CSNPs. The reset may be performed multiple times. If the expiry count of the T1 timer exceeds the threshold value, the GR Restarter forcibly cancels the T1 timer and starts normal IS-IS processing.
Fast Convergence
Routing Control
Other Features
Notes: Notes:
  In Step 2, if the neighbor does not have the GR Helper capability, it ignores the Restart TLV and resets the adjacency with the GR Restarter according to normal IS-IS processing.
  In Step 3, the Restarter sets the value of the T3 timer to the Holdtime of the neighbor, preventing neighbor disconnection during the GR, which would otherwise cause routes to be recalculated on the whole network.

## Slide 89: IS-IS GR Process (Restarting) (2)
The GR process triggered by an active/standby switchover or the restart of an IS-IS process is referred to as restarting, in which the FIB remains unchanged.
After the GR Restarter cancels the T1 timers on all interfaces, clears the CSNP list, and collects all LSPs, it considers the synchronization with all neighbors complete and cancels the T2 timer.
The cancellation of the T2 timer indicates that LSDBs of the corresponding level are synchronous.
  In the case of a single-level device, the SPF calculation is triggered directly.
  In the case of a Level-1-2 device, the device checks whether the T2 timer of the other level is also canceled. If the T2 timers of both levels are canceled, SPF calculation is triggered. Otherwise, the device waits for the T2 timer of the other level to expire.
After the T2 timers of both levels are canceled, the GR Restarter cancels the T3 timer and updates its FIB. The GR Restarter re-generates the LSPs of each level and floods them. During synchronization, if the GR Restarter receives the LSPs that were generated by itself before the restarting, it deletes them.
At this point, the IS-IS restarting of the GR Restarter is complete.
GR Restarter
GR Helper
R1
R2
GR Session
IIH (Restart TLV: RR=1, RA=0, SA=0)
CSNP
LSP flooding
LSPs
Active/standby switchover
Starts T1, T2, and T3 timers.
Updates the FIB.
IIH (Restart TLV: RR=0, RA=1, SA=0)
Resets the T3 timer.
Cancels the T1 timer.
Cancels the T2 timer.
Cancels the T3 timer.
Updates the FIB.
Fast Convergence
Routing Control
Other Features
Notes: During the restarting, the Restarter starts the T1, T2, and T3 timers at the same time after the protocol restart. The value of the T1 timer indicates the longest time during which the GR Restarter waits for the Hello packet used for GR acknowledgement from the GR Helper. The value of the T2 timer indicates the longest time during which the system waits for the LSDB synchronization. The value of the T3 timer indicates the longest time allowed for a GR. The device cancels the T3 timer after synchronization of Level-1 and Level-2 LSDBs completes during the GR. If LSDB synchronization has not completed when the T3 timer expires, the GR fails.

## Slide 90: IS-IS GR Process (Starting) (1)
The GR process triggered by a device restart is referred to as starting, in which the FIB is updated.
GR Restarter
GR Helper
R1
R2
GR Session
IIH (Restart TLV: RR=0, RA=0, SA=1)
LSP flooding
Starts the T2 timer.
Updates the FIB.
Adjacency reestablishment
Cancels the T2 timer.
Updates the FIB.
As a starting device does not retain its FIB, it wants the neighbors with which the adjacencies are up before the device starts, to reset the adjacencies and suppress advertisement of the adjacencies in a period.
After the GR Restarter starts, it performs the following actions:
  Starts one T2 timer for synchronization of LSDBs at each level.
  Sends IIH packets that contain the Restart TLV through all interfaces. In the packets, RR is cleared, and SA is set.
After receiving an IIH packet that carries the Restart TLV, a neighbor performs the following actions based on whether GR is supported:
  If GR is supported, the neighbor re-initiates the adjacency.
  If GR is not supported, the neighbor ignores the Restart TLV and resets the adjacency with the GR Restarter.
After adjacencies are re-initiated, the GR Restarter re-establishes them with neighbors on each interface. When an adjacency goes up, the GR Restarter starts the T1 timer for the interface.
IIH (Restart TLV: RR=1, RA=0, SA=1)
IIH (Restart TLV: RR=0, RA=1, SA=0)
Starting
CSNP
LSPs
.
.
.
Starts the T1 timer.
Cancels the T1 timer.
Starts to synchronize LSDBs.
Fast Convergence
Routing Control
Other Features
Notes: Additional remarks for Step 1:
  If RR is cleared, starting has completed.
  The IIH packet in which SA is set indicates that the Restarter requests its neighbor to suppress the advertisement of their adjacency until the neighbor receives an IIH packet in which SA is cleared from the Restarter.
Additional remarks for Step 2:
  If GR is supported, the neighbor re-initiates the adjacency with the GR Restarter and deletes the description of the adjacency from the LSPs to be sent. In addition, the neighbor ignores the link connected to the GR Restarter when performing SPF calculation until it receives an IIH packet in which SA is cleared from the GR Restarter.
  If GR is not supported, the neighbor ignores the Restart TLV, resets the adjacency with the GR Restarter, replies with an IIH packet that does not contain the Restart TLV, and returns to normal IS-IS processing. In this case, the neighbor does not suppress the advertisement of the adjacency with the GR Restarter. In the case of a P2P link, the neighbor also sends a CSNP.

## Slide 91: IS-IS GR Process (Starting) (2)
The GR process triggered by a device restart is referred to as starting, in which the FIB is updated.
When the T1 timer expires, the GR Restarter sends an IIH packet in which both RR and SA are set.
After the neighbor receives the IIH packet in which both RR and SA are set, it replies with an IIH packet, in which RR is cleared and RA is set, and sends a CSNP.
After receiving the IIH packet used for acknowledgement and CSNP from the neighbor, the GR Restarter cancels the T1 timer.
If the GR Restarter does not receive an IIH packet or CSNP, it constantly resets the T1 timer and resends the IIH packet in which RR and SA are set. If the expiry count of the T1 timer exceeds the threshold value, the GR Restarter forcibly cancels the T1 timer and starts normal IS-IS processing to perform LSDB synchronization.
After receiving the CSNP from the Helper, the GR Restarter starts LSDB synchronization.
After LSDBs of a level are synchronized, the GR Restarter cancels the corresponding T2 timer.
After all T2 timers are canceled, SPF calculation is started and LSPs are regenerated and flooded.
At this point, the IS-IS starting of the GR Restarter is complete.
GR Restarter
GR Helper
R1
R2
GR Session
IIH (Restart TLV: RR=0, RA=0, SA=1)
LSP flooding
Starts the T2 timer.
Updates the FIB.
Adjacency reestablishment
Cancels the T2 timer.
Updates the FIB.
IIH (Restart TLV: RR=1, RA=0, SA=1)
IIH (Restart TLV: RR=0, RA=1, SA=0)
Starting
CSNP
LSPs
.
.
.
Starts the T1 timer.
Cancels the T1 timer.
Starts to synchronize LSDBs.
Fast Convergence
Routing Control
Other Features

## Slide 92: Configuring IS-IS GR (1)
[Huawei-isis-1] graceful-restart
Enable IS-IS GR.
[Huawei-isis-1] graceful-restart no-impact-holdtime
Configure the device to remain the IS-IS neighbor Holdtime unchanged in GR scenarios.
By default, after IS-IS GR is enabled, the IS-IS neighbor Holdtime is automatically changed to 60s if it is less than 60s, and the Holdtime remains unchanged if it is greater than or equal to 60s.
[Huawei-isis-1] graceful-restart interval interval-value
(Optional) Configure a value for the T3 timer used in an IS-IS GR.
By default, the GR T3 timer is 300s.
(Optional) Configure a value for the T2 timer used in an IS-IS GR.
[Huawei-isis-1] graceful-restart t2-interval interval-value
By default, the GR T2 timer is 60s.
Fast Convergence
Routing Control
Other Features
Notes: Usage scenario of the graceful-restart no-impact-holdtime command:
  On an IS-IS network, if GR is configured on a device, its IS-IS neighbors may automatically update corresponding neighbor Holdtimes. Specifically, the Holdtimes are changed to 60s if they are less than 60s, and remain unchanged if they are greater than or equal to 60s. Consequently, the minimum Holdtime value is 60s after the update. If one of the neighbors fails in non-GR scenarios, it takes at least 60s for the other end to detect the failure. As a result, a large number of packets may be discarded within this period, reducing network security and reliability.
  To resolve this problem, you can run the graceful-restart no-impact-holdtime command so that the Holdtimes of neighbors remain unchanged in an IS-IS GR scenario. In this way, neighbor status can be fast detected, implementing rapid network convergence.
graceful-restart interval interval-value and graceful-restart t2-interval interval-value commands
  interval interval-value: specifies a value of the GR T3 or T2 timer. The value is an integer that ranges from 30 to 1800, in seconds.
  It is recommended that the value of the T3 timer is greater than that of the T2 timer. Otherwise, the GR may fail.

## Slide 93: Configuring IS-IS GR (2)
[Huawei-isis-1] graceful-restart suppress-sa
(Optional) Configure the GR Restarter to suppress the SA bit in the Restart TLV.
[Huawei] display isis process-id graceful-restart status [ level-1 | level-2 ]
Display the IS-IS GR status.
[Huawei] display isis graceful-restart status [ level-1 | level-2 ] [ process-id | vpn-instance vpn-instance-name ]
level-1: displays the Level-1 IS-IS GR status.
level-2: displays the Level-2 IS-IS GR status.
process-id: displays the IS-IS GR status of a specified IS-IS process. The value is an integer ranging from 1 to 65535.
vpn-instance vpn-instance-name: displays the IS-IS GR status of a specified VPN instance in an IS-IS multi-instance process. The value is a string of 1 to 31 case-sensitive characters. It cannot contain spaces. The character string can contain spaces if it is enclosed with double quotation marks (").
Fast Convergence
Routing Control
Other Features
Notes: Usage scenario of the graceful-restart suppress-sa command:
  A router does not maintain the forwarding status when it starts for the first time (excluding the post-GR cases). If it is not the first time that a router has started, the LSPs generated when the router ran last time may still exist in the LSP database of other routers on the network.
  Because the sequence numbers of LSP fragments are also reinitialized when the router starts, the LSP copies stored on other routers seem to be newer than the LSPs generated after the local router starts. This leads to a temporary "blackhole" on the network, and the blackhole persists until the router regenerates its own LSPs and advertises them with the largest sequence number.
  If the neighbors of the router are suppressed from advertising adjacencies to the router during the startup of the router until the router advertises updated LSPs, the preceding problem can be prevented. Therefore, you can run the graceful-restart suppress-sa command to suppress the SA bit in the Restart TLV.

## Slide 94: Example for Configuring IS-IS GR (1)
Routers R1 and R2 each are equipped with two main control boards, which back up each other. The routers interwork through IS-IS and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an IS-IS process or performs an active/standby switchover in GR mode.
IS-IS area 10
R1
10.1.12.0/30
R2
GE0/0/0
1. Assign an IP address to each involved interface and configure IS-IS on each device. The configuration details are omitted.
[R1] isis 1
[R1-isis-1] graceful-restart
[R1-isis-1] graceful-restart no-impact-holdtime
.1
.2
[R2] isis 1
[R2-isis-1] graceful-restart
[R2-isis-1] graceful-restart no-impact-holdtime
2. Enable IS-IS GR on R1 and R2.
Fast Convergence
Routing Control
Other Features

## Slide 95: Example for Configuring IS-IS GR (2)
Routers R1 and R2 each are equipped with two main control boards, which back up each other. The routers interwork through IS-IS and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an IS-IS process or performs an active/standby switchover in GR mode.
IS-IS area 10
R1
10.1.12.0/30
R2
GE0/0/0
3. Check the IS-IS GR status on R2.
.1
.2
<R2> display isis 1 graceful-restart status
Restart information for ISIS(1)
-------------------------------
IS-IS(1) Level-1 Restart Status
Restart Interval: 300
SA Bit Supported
Total Number of Interfaces = 1
Restart Status: RESTART COMPLETE
IS-IS(1) Level-2 Restart Status
Restart Interval: 300
SA Bit Supported
Total Number of Interfaces = 1
Restart Status: RESTART COMPLETE
Fast Convergence
Routing Control
Other Features

## Slide 96: Example for Configuring IS-IS GR (3)
Routers R1 and R2 each are equipped with two main control boards, which back up each other. The routers interwork through IS-IS and support GR.
It is required that traffic forwarding be not interrupted when R1 restarts an IS-IS process or performs an active/standby switchover in GR mode.
IS-IS area 10
R1
10.1.12.0/30
R2
GE0/0/0
4. Run the reset isis all graceful-restart command in the user view of R1 to restart IS-IS process 1, and run the display isis peer command on R2 to check the IS-IS adjacency with R1.
.1
.2
<R1> reset isis 1 all graceful-restart
<R2> display fib
Route Flags: G - Gateway Route, H - Host Route, U - Up Route
S - Static Route, D - Dynamic Route, B - Black Hole Route
L - Vlink Route
--------------------------------------------------------------------------------
FIB Table:
Total number of Routes : 7
Destination/Mask Nexthop Flag TimeStamp Interface TunnelID
10.1.12.3/32 127.0.0.1 HU t[15] InLoop0 0x0
10.1.12.2/32 127.0.0.1 HU t[15] InLoop0 0x0
255.255.255.255/32 127.0.0.1 HU t[3] InLoop0 0x0
127.255.255.255/32 127.0.0.1 HU t[3] InLoop0 0x0
127.0.0.1/32 127.0.0.1 HU t[3] InLoop0 0x0
127.0.0.0/8 127.0.0.1 U t[3] InLoop0 0x0
10.1.12.0/30 10.1.12.2 U t[15] GE0/0/0 0x0
When R1 restarts the IS-IS process in GR mode, the FIB remains unchanged, ensuring uninterrupted data forwarding.
Fast Convergence
Routing Control
Other Features

## Slide 97
(Multiple-answer question) Which of the following fast convergence mechanisms are supported by OSPF? ( )
  PRC
  LSP fast flooding
  Intelligent timer
  OSPF IP FRR
(True or false) The FA field in Type 5 LSAs of OSPF must be 0.0.0.0. ( )
  True
  False
Notes: ACD
B

## Slide 98
(True or false) On an IS-IS network, if a device runs mode-2 LSP fragment extension, virtual systems do not participate in SPF calculation. All routers on the network know that the LSPs generated by the virtual systems actually belong to the originating system. ( )
  True
  False
Notes: A

## Slide 99
To better adapt to network topology changes, OSPF and IS-IS support multiple fast convergence modes. I-SPF and PRC algorithms speed up route calculation; FRR enables fast traffic switching to the backup link; and intelligent timers allow you to control the speeds at which link state information is generated and routes are calculated.
To control the size of routing tables and improve network performance, OSPF and IS-IS support route filtering, equal-cost routes, and delivery of default routes. To isolate protocol routing tables, OSPF and IS-IS support multi-process deployment on the same device. Routing tables of different processes are independent of each other.
To prevent a suboptimal route from being selected when external routes are imported, OSPF uses the FA in Type 5 or Type 7 LSAs to guide data packet forwarding. To carry more routing information, IS-IS supports LSP fragment extension.
To ensure that key services are not interrupted during a device restart, OSPF and IS-IS also support GR and NSR.
Thanks to the preceding features, OSPF and IS-IS are widely and flexibly used on live networks.