## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2020.06.15
Li Xianzhi/00354681
New
Lu Yueyue/WX445705
2021.10.15
He Junjian/WX580230
Update

## Slide 2: Advanced BGP Features

## Slide 3
Border Gateway Protocol (BGP) is usually deployed on large-scale networks. Compared with an Interior Gateway Protocol (IGP), BGP has more flexible route control capabilities. Each BGP route can carry multiple path attributes. Special route matching tools, such as AS_Path and community filters, are available for filtering routes based on the route attributes. Routing policies can be used to control route advertisement and acceptance according to the actual networking requirements.
In addition, BGP provides various advanced features and networking deployment solutions to improve network performance.
This course describes the fundamentals and configurations of BGP route control, common advanced BGP features, such as ORF, peer group, security features, and 4-byte AS number, as well as the networking modes of BGP route reflectors (RRs).

## Slide 4
On completion of this course, you will be able to:
  Use regular expressions when configuring AS_Path and community filters.
  Use AS_Path and community filters to control BGP routes.
  Apply the ORF and peer group functions of BGP.
  Perform basic configurations of BGP security.
  Describe the concepts related to 4-byte AS numbers and usage.
  Describe the networking modes of BGP RRs.

## Slide 5
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 6: Overview of BGP Route Control
BGP route control involves controlling the advertisement and acceptance of routes.
Generally, BGP route control is implemented using routing policies. Specifically, a route matching tool is used to match specific routes, and then a routing policy tool is used to control route advertisement and acceptance.
  Route matching tools: access control list (ACL), IP prefix list, AS_Path filter, and community filter
  Routing policy tools: filter-policy and route-policy
BGP controls routes by matching attributes such as AS_Path and Community.
Overview
AS_Path Filter
Community Filter
AS 102
AS 101
R1
Net1
Net2
Net3
R2
R3
R4
BGP Routing-table
*> Net1
*> Net3
BGP Routing-table
*> Net1
*> Net2
*> Net3
BGP Routing-table
*> Net1 (R3 is preferred as the egress)
*> Net3
Filter out the Net2 route.
Modify the attributes of the Net1 and Net3 routes to control route selection.
Modify the attributes of the Net1 and Net3 routes to control route selection.
Route
Route
Route
BGP Routing-table
*> Net1
*> Net3 (R4 is preferred as the egress)
Notes: As shown in the figure:
  R1 and R2 reside in AS 101, and establish an IBGP peer relationship with each other. R3 and R4 reside in AS 102, and each establishes an EBGP peer relationship with R2.
  R1 is directly connected to three subnets: Net1, Net2, and Net3. R1 advertises routes to the three subnets to its BGP routing table.
  R2 can filter out the Net2 route through BGP route control so that R2's BGP routing table does not contain the Net2 route.
  R3 and R4 can implement BGP route control by modifying the attributes of the Net1 and Net3 routes, respectively. In this way, when a device in AS 102 accesses Net1, R3 is preferentially selected as the egress device; when the device accesses Net3, R4 is preferentially selected as the egress device.
Note: For details about the ACL, IP prefix list, filter-policy, route-policy, and BGP path attributes, see the "HCIP-Datacom-Core Technology" course.

## Slide 7: Regular Expression
A regular expression (regex) is a formula used to match character strings based on a specific template. It consists of common characters (for example, letters from a to z) and special characters.
Common characters are used to match themselves in a string:
  Include all upper-case and lower-case letters, digits, punctuations, and special symbols.
  For example, the regex a matches the letter "a" in "abc", the regex 10 matches the digits "10" in "10.113.25.155", and the regex @ matches the symbol "@" in "xxx@xxx.com".
Special characters, together with common characters, are used to match complex or special character strings:
  A special character that precedes or follows a common character is used to restrict or extend the independent control character or placeholder of the common character.
  A special character describes how the character that precedes the special character is reused.
  A special character specifies a complete range.
Overview
AS_Path Filter
Community Filter
Notes: A regex has the following functions:
  Checks and obtains the sub-character string that matches a specific rule in the character string.
  Replaces the character string based on matching rules.

## Slide 8: Example of Special Characters (1)
Type 1
. | Matches any single character, including a space. | 0.0 matches 0x0, 020, and so on.
^ | Matches the start position of a character string. | ^10 matches 10.1.1.1 but not 20.1.1.1.
$ | Matches the end position of a character string. | 1$ matches 10.1.1.1 but not 10.1.1.2.
_ | Underscore, which matches any separator. Matches a comma (,), left brace ({), right brace (}), left parenthesis ((), or right parenthesis ()). (Same as ^) Matches the start position of an input character string. (Same as $) Matches the end position of an input character string. Matches a space. | _10 matches (10, {10, space10, and so on. 10_ matches 10), 10}, 10space, and so on.
¦ | Pipeline character, which is a logical OR operator. x¦y matches x or y. | 100¦200 matches 100 or 200.
\ | Defines an escape character, which is used to mark the next character (common or special character) as a common character. | \* matches *.
* | Matches a sub-regular expression that it follows zero or multiple times. | 10* matches 1, 10, 100, 1000, and so on. | (10) * matches null, 10, 1010, 101010, and so on.
+ | Matches a sub-regular expression that it follows once or multiple times. | 10+ matches 10, 100, 1000, and so on. | (10)+ matches null, 10, 1010, 101010, and so on.
? | Matches a sub-regular expression that it follows zero times or once. | 10? matches 1 or 10. | (10)? matches null or 10.
Type 2
Overview
AS_Path Filter
Community Filter
Notes: Note: The parentheses () can be used to define the scope and priority of an operator. For example, gr(a|e)y is equivalent to gray|grey.

## Slide 9: Example of Special Characters (2)
Type 3
[xyz] | Matches any character contained in a regex. | [123] matches the character 2 in 255.
[^xyz] | Matches any character that is not contained in a regex. | [^123] matches any character except 1, 2, and 3.
[a-z] | Matches any character within a specified range in a regex. | [0-9] matches all digits in the range from 0 to 9.
[^a-z] | Matches any character beyond the range specified in a regex. | [^0-9] matches all non-digit characters (matching any characters except digits 0 to 9).
Think about character strings that can be matched against the regexes of the following types.
  Type 1 Type 2 Type 3
^a.$
^100_
^100$
100$|400$
^\(65000\)$
abc*d
abc+d
abc?d
a(bc)?d
[abcd]
[a-c 1-2]$
[^act]$
[123].[7-9]
Overview
AS_Path Filter
Community Filter
Notes: Type 1:
  ^a.$: matches a character string that starts with the character a and ends with any single character, for example, a0, a!, ax, and so on.
  ^100_: matches a character string starting with 100, for example, 100, 100 200, 100 300 400, and so on.
  ^100$: matches only 100.
  100$|400$: matches a character string ending with 100 or 400, for example, 100, 1400, 300 400, and so on.
  ^\(65000\)$: matches (65000) only.
Type 2:
  abc*d: matches the character c zero or multiple times, for example, abd, abcd, abccd, abcccd, abccccdef, and so on.
  abc+d: matches the character c once or multiple times, for example, abcd, abccd, abcccd, abccccdef, and so on.
  abc?d: matches the character c zero times or once, for example, abd, abcd, abcdef, and so on.
  a(bc)?d: matches the character string bc zero times or once, for example, ad, abcd, aaabcdef, and so on.

## Slide 10
Notes: Type 3:
  [abcd]: matches any character in the string abcd, for example, ax, b!, abc, d0, and so on.
  [a-c 1-2]$: matches a character string ending with any of a, b, c, 1, and 2, for example, a, a1, 62, xb, 7ac, and so on.
  [^act]$: matches a character string that does not end with a, c, or t, for example, ax, b!, d, and so on.
  [123].[7-9]: matches the character strings such as 1 7, 2x9, and 348.

## Slide 11: Route Matching Tool: AS_Path Filter
An AS_Path filter uses the AS_Path attribute of BGP routes as a matching condition to filter BGP routes.
If you do not want routes from certain ASs, you can use an AS_Path filter to filter out the routes that carry the associated AS numbers.
AS 104
AS 103
AS 102
AS 101
R1
10.1.1.0/24
R2
10.1.1.0/24
AS_Path=101
Route
10.1.1.0/24
AS_Path=102 101
The BGP route originated from AS 101 is filtered out.
Route
Route
Set an AS_Path filter to filter out the BGP route that contains the AS number 101.
Overview
AS_Path Filter
Community Filter
Notes: The AS_Path attribute is a well-known mandatory attribute of BGP. All BGP routes must carry this attribute. This attribute records the numbers of all the ASs that a BGP route traversed during transmission.
The value of the AS_Path attribute can be 0, 1, or a set of multiple AS numbers.

## Slide 12: Using a Regex to Match the AS_Path Attribute
A regex can be used to match the AS_Path attribute of routes.
  For example, a regex can match the AS number 103 in AS_Path = 103 102 101.
You can use different regexes to meet different requirements, for example, using ^101$ to match AS 101, and _101$ to match the AS_Path lists ending with AS 101.
AS 104
Route
10.1.12.0/24 AS_Path = 103 102 101
10.1.15.0/24 AS_Path = 103 105 101
10.1.78.0/24 AS_Path = 103 107 108
...
R1
R1 receives many BGP routes, each of which has its own AS_Path value.
To meet a specific requirement, R1 needs to apply a policy to the routes carrying the AS number 101 in their AS_Path attribute. In this case, you can associate an AS_Path filter with a regex to match routes, regardless of the route prefixes.
AS_Path:
Character string:
Regex:
Other examples:
^$ | Matches the AS_Path list that does not contain any AS number, that is, matching routes in the local AS.
.* | Matches all or any routes.
^10[012349]$ | Matches the AS numbers 100, 101, 102, 103, 104, and 109.
^10[^0-6]$ | Matches the AS_Path lists that exclude the AS numbers 100 to 106.
^10. | Matches the AS numbers 100 to 109 and 10.
^12(_34)?_56$ | Matches the AS_Path lists 12 56 and 12 34 56.
103
102
101
103
102
101
^103，^103_ and so on.
Overview
AS_Path Filter
Community Filter

## Slide 13: Basic AS_Path Filter Configuration Commands
Create an AS_Path filter.
An AS_Path filter uses a regex to define a matching rule.
Note: The default behavior of an AS_Path filter is deny.
Apply the AS_Path filter.
A routing policy associated with the AS_Path filter is applied to BGP routes in the BGP address family view to filter out the unqualified routes.
A matching rule based on the AS_Path filter is created in the route-policy view.
[Huawei] ip as-path-filter { as-path-filter-number | as-path-filter-name } { deny | permit } regular-expression
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address | ipv6-address } as-path-filter { as-path-filter-number | as-path-filter-name } { import | export }
[Huawei-route-policy] if-match as-path-filter { as-path-filter-number | as-path-filter-name }
Overview
AS_Path Filter
Community Filter
Notes: Multiple matching rules (each in permit or deny mode) can be specified in an AS_Path filter. These rules are in the OR relationship, which means that if a route matches one of the matching rules, the route is considered to match the AS_Path filter.
Command: [Huawei] ip as-path-filter {as-path-filter-number | as-path-filter-name} {deny | permit} regular-expression
  as-path-filter-number: specifies the number of an AS_Path filter. The value is an integer ranging from 1 to 256.
  as-path-filter-name: specifies the name of an AS_Path filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits. If spaces are used, the string must start and end with double quotation marks (").
  deny: sets the matching mode of the AS_Path filter to deny.
  permit: sets the matching mode of the AS_Path filter to permit.
  regular-expression: specifies a regex for the AS_Path filter. The value is a string of 1 to 255 characters and can contain spaces.
The default behavior of an AS_Path filter is deny. That is, if a route is not permitted in a filtering, the route fails to match the AS_Path filter. If all matching rules in an AS_Path filter work in deny mode, all BGP routes are denied by the filter. To prevent this problem, configure a matching rule in permit mode after one or more matching rules in deny mode so that the routes except for those denied by the preceding matching rules can be permitted by the filter.

## Slide 14: Examples for Configuring AS_Path Filters (1)
R2 transmits EBGP routes to R3. Among these routes, some are locally originated by R2, and the others are transmitted from AS 101 to R2 and then updated by R2 to R3.
A routing policy is configured on R2 to deny the routes originated from AS 101.
1. Create an AS_Path filter.
2. (Direct reference) Apply the AS_Path filter.
The AS_Path filter is configured to filter out the routes originated from AS 101 and permit the other routes.
Route filtering
AS 104
AS 101
AS 102
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0：
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
AS 103
[R2] ip as-path-filter 1 deny _101$
[R2] ip as-path-filter 1 permit .*
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 as-number 103
[R2-bgp] ipv4-family unicast
[R2-bgp-af-ipv4] peer 10.1.23.3 as-path-filter 1 export
Overview
AS_Path Filter
Community Filter

## Slide 15: Examples for Configuring AS_Path Filters (2)
1. Create an AS_Path filter.
2. (Through a route-policy) Apply the AS_Path filter.
The AS_Path filter is configured to filter out the routes originated from AS 101 and permit the other routes.
R2 transmits EBGP routes to R3. Among these routes, some are locally originated by R2, and the others are transmitted from AS 101 to R2 and then updated by R2 to R3.
A routing policy is configured on R2 to deny the routes originated from AS 101.
Route filtering
AS 104
AS 101
AS 102
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0：
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
AS 103
[R2] route-policy AS_Path permit node 10
[R2-route-policy] if-match as-path-filter 1
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 as-number 103
[R2-bgp] ipv4-family unicast
[R2-bgp-af-ipv4] peer 10.1.23.3 route-policy AS_Path export
[R2] ip as-path-filter 1 deny _101$
[R2] ip as-path-filter 1 permit .*
Overview
AS_Path Filter
Community Filter

## Slide 16: Checking the AS_Path Filter Information
1. Check the AS_Path filter.
2. Check all the routes whose AS_Path lists match the specified regex in the BGP routing table.
The route 10.1.1.1/32 originated from AS 101 is filtered by the AS_Path filter.
Route filtering
AS 104
AS 101
AS 102
R1
R2
R4
R3
Route
10.1.34.0/24
.2
.3
Loopback0：
10.1.1.1/32
10.1.12.0/24
.1
.2
.4
.3
10.1.23.0/24
AS 103
[R2]display ip as-path-filter 1
As path filter number: 2
deny _101$
permit .*
[R2]display bgp routing-table regular-expression _101$
Total Number of Routes: 1
BGP Local router ID is 10.1.12.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.1.1/32 10.1.12.1 0 0 101i
Overview
AS_Path Filter
Community Filter

## Slide 17: Route Matching Tool: Community Filter
The community filter and community attribute can be used together to simplify route management when the IP prefix list and AS_Path filter are not available.
There are two types of community filters:
  Basic community filter, which matches the community number or well-known community attribute.
  Advanced community filter, which uses a regex to match the community number.
AS 102
AS 103
AS 101
R1
10.1.1.0/24
10.1.2.0/24
R2
10.1.1.0/24 with community 101:1
10.1.2.0/24 without the community attribute
Route
Route
Set a community filter to deny the routes whose community value is 101:1.
10.1.2.0/24
The route 10.1.1.0/24 with community 101:1 is filtered out.
R3
Overview
AS_Path Filter
Community Filter
Notes: The community attribute is an optional transitive attribute. It can identify the routes with the same characteristics, regardless of the scattered route prefixes and various AS numbers. That is, a specific community value can be assigned to some routes so that these routes can be matched against the community value instead of the network number or mask. Then, a corresponding routing policy can be applied to the matched routes.

## Slide 18: Community Attributes
Well-known community attributes
Name | Number | Description
Internet | 0 (0x00000000) | After a device receives a route with this attribute, the device can advertise this route to any BGP peer. By default, all routes belong to the Internet community.
No_Advertise | 4294967042 (0xFFFFFF02) | After a device receives a route with this attribute, the device does not advertise this route to any BGP peer.
No_Export | 4294967041 (0xFFFFFF01) | After a device receives a route with this attribute, the device does not advertise this route outside the local AS.
No_Export_Subconfed | 4294967043 (0xFFFFFF03) | After a device receives a route with this attribute, the device does not advertise this route outside the local AS. If a confederation is used, the device does not advertise this route to the other sub-ASs in the confederation.
Community attribute format:
  The length of a community attribute is 32 bits, which can be presented in either of the following formats:
    Decimal integer
    In the AA:NN format, AA indicates an AS number, and NN is a user-defined number.
Overview
AS_Path Filter
Community Filter

## Slide 19: Basic Community Configuration Commands
Set a community value or multiple community values for the matched routes in a route-policy.
Configure the device to advertise the community attribute(s) to a specified peer or peer group.
By default, a device advertises no community attribute to its peer or peer group.
[Huawei-route-policy] apply community { community-number | aa:nn | internet | no-advertise | no-export | no-export-subconfed } [ additive ]
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address | ipv6-address } advertise-community
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei-route-policy] apply community { community-number | aa:nn | internet | no-advertise | no-export | no-export-subconfed } [ additive ]
  community-number | aa:nn: specifies a community number for a community attribute. A maximum of 32 community numbers can be specified at a time using this command. The value of community-number is an integer ranging from 0 to 4294967295. The values of aa and nn are also integers ranging from 0 to 65535.
  internet: allows the matched routes to be advertised to any peers. By default, all routes belong to the Internet community.
  no-advertise: prevents the matched routes from being advertised to any peer. After a device receives a route with this attribute, it cannot advertise this route to any other BGP peers.
  no-export: prevents the matched routes from being advertised outside the local AS but allows them to be advertised to other sub-ASs in the local AS. After a device receives a route with this attribute, it cannot advertise this route outside the local AS.
  no-export-subconfed: prevents the matched routes from being advertised outside the local AS or to other sub-ASs in the local AS. After a device receives a route with this attribute, it cannot advertise this route to any other sub-ASs.
  additive: adds community attributes to the routes that match the filtering conditions.

## Slide 20: Basic Community Filter Configuration Commands (1)
Create a basic community filter.
Create an advanced community filter.
The number of an advanced community filter ranges from 100 to 199. A regex can be specified as a matching condition in an advanced community filter.
The number of a basic community filter ranges from 1 to 99. Only the community number or well-known community attribute can be specified in a basic community filter.
[Huawei] ip community-filter { basic comm-filter-name | basic-comm-filter-num } { permit | deny } [ community-number | aa:nn | internet | no-export-subconfed | no-advertise | no-export ]
[Huawei] ip community-filter { advanced comm-filter-name | adv-comm-filter-num } { permit | deny } regular-expression
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei] ip community-filter { basic comm-filter-name | basic-comm-filter-num } { permit | deny } [ community-number | aa:nn | internet | no-export-subconfed | no-advertise | no-export ]
  basic comm-filter-name: specifies the name of a basic community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits.
  basic-comm-filter-num: specifies the number of a basic community filter. The value is an integer ranging from 1 to 99.
  deny: sets the matching mode of the community filter to deny.
  permit: sets the matching mode of the community filter to permit.
  community-number: specifies a community number. The value is an integer ranging from 0 to 4294967295.
  aa:nn: specifies a community number. A maximum of 20 community numbers can be specified at a time using this command. The values of aa and nn are integers ranging from 0 to 65535.
  internet: allows the matched routes to be advertised to any peers.
  no-export-subconfed: prevents the matched routes from being advertised outside the local AS. If a confederation is used, the matched routes will not be advertised to the other sub-ASs in the confederation.
  no-advertise: prevents the matched routes from being advertised to any other peers.
  no-export: prevents the matched routes from being advertised outside the local AS. If a confederation is used, the matched routes will not be advertised outside the confederation but will be advertised to the other sub-ASs in the confederation.

## Slide 21
Notes: Command: [Huawei] ip community-filter { advanced comm-filter-name | adv-comm-filter-num } { permit | deny } regular-expression
  advanced comm-filter-name: specifies the name of an advanced community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits.
  adv-comm-filter-num: specifies the number of an advanced community filter. The value is an integer ranging from 100 to 199.
  regular-expression: specifies a regex for the community filter. The value is a string of 1 to 255 case-sensitive characters and can contain spaces.

## Slide 22: Basic Community Filter Configuration Commands (2)
Apply a community filter.
A matching rule based on the community filter is created in the route-policy view.
[Huawei-route-policy] if-match community-filter { basic-comm-filter-num [ whole-match ] | adv-comm-filter-num }
[Huawei-route-policy] if-match community-filter comm-filter-name [ whole-match ]
Overview
AS_Path Filter
Community Filter
Notes: Command: [Huawei-route-policy] if-match community-filter { basic-comm-filter-num [ whole-match ] | adv-comm-filter-num }
Command: [Huawei-route-policy] if-match community-filter comm-filter-name [ whole-match ]
  basic-comm-filter-num: specifies the number of a basic community filter. The value is an integer ranging from 1 to 99.
  adv-comm-filter-num: specifies the number of an advanced community filter. The value is an integer ranging from 100 to 199.
  comm-filter-name: specifies the name of a community filter. The value is a string of 1 to 51 case-sensitive characters. It cannot be comprised of only digits. If spaces are used, the string must start and end with double quotation marks (").
  whole-match: indicates complete matching. That is, all the community attributes in the specified community filter must be matched. This parameter applies only to basic community filters.

## Slide 23: Examples for Configuring Community Filters
Example for configuring a basic community filter.
Match the routes carrying community values [100:1, 200:1, 300:1]. (The relationship between multiple community values in a command configuration is AND.)
Match the routes carrying community value [100:1] or community values [200:1, 300:1]. (The relationship between different groups of community values is OR. A set of community values in a command configuration is called a group.)
Example for configuring an advanced community filter.
Match the routes carrying community values starting with 10.
ip community-filter 1 permit 100:1 200:1 300:1
ip community-filter 1 permit 100:1
ip community-filter 1 permit 200:1 300:1
ip community-filter 100 permit ^10
Overview
AS_Path Filter
Community Filter

## Slide 24: Configuring Community Attributes (1)
1. Configure a routing policy on R1 to add a community attribute to matched routes, and enable R1 to advertise the community attribute to the EBGP peer R2.
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
AS 101
AS 102
AS 103
R1
R2
R3
10.1.1.1/32 Community=101:1
10.1.2.2/32
Loopback0:
10.1.1.1/32
Loopback1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
[R1] ip ip-prefix 1 permit 10.1.1.1 32
[R1] route-policy Community permit node 10
[R1-route-policy] if-match ip-prefix 1
[R1-route-policy] apply community 101:1
[R1-route-policy] quit
[R1] route-policy Community permit node 20
[R1-route-policy] quit
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] peer 10.1.12.2 route-policy Community export
[R1-bgp] peer 10.1.12.2 advertise-community
[R1-bgp] network 10.1.1.1 32
[R1-bgp] network 10.1.2.2 32
Overview
AS_Path Filter
Community Filter
Notes: Command: [R1] route-policy Community permit node 20
Run this command to allow the route 10.1.2.2/32 to be advertised properly.

## Slide 25: Configuring Community Attributes (2)
2. Configure R2 to advertise the community attribute to the EBGP peer R3.
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
Configure a routing policy on R2 to allow the community attribute no-expert to be added to the BGP route 10.1.1.1/32 when R2 advertises this route.
AS 101
AS 102
AS 103
R1
R2
R3
Loopback0:
10.1.1.1/32
Loopback1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
10.1.1.1/32 Community=101:1 no-export
10.1.2.2/32
[R2] ip ip-prefix 1 permit 10.1.1.1 32
[R2] route-policy Community permit node 10
[R2-route-policy] if-match ip-prefix 1
[R2-route-policy] apply community no-expert additive
[R2-route-policy] quit
[R2] route-policy Community permit node 20
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] peer 10.1.23.3 as-number 102
[R2-bgp] peer 10.1.23.3 advertise-community
[R2-bgp] peer 10.1.23.3 route-policy Community export
Overview
AS_Path Filter
Community Filter

## Slide 26: Configuring Community Attributes (3)
3. Check the BGP routing information on R3.
Configure a routing policy on R1 to allow the community value 101:1 to be carried only in the BGP route 10.1.1.1/32 when R1 advertises this route.
Configure a routing policy on R2 to allow the community attribute no-expert to be added to the BGP route 10.1.1.1/32 when R2 advertises this route.
AS 101
AS 102
AS 103
R1
R2
R3
Loopback0:
10.1.1.1/32
Loopback1:
10.1.2.2/32
10.1.12.0/24
.1
.2
10.1.23.0/24
.2
.3
10.1.1.1/32 Community=101:1 no-export
10.1.2.2/32
[R3] bgp 103
[R3-bgp] peer 10.1.23.2 as-number 102
[R3-bgp] quit
[R3] display bgp routing-table 10.1.1.1
BGP local router ID : 10.1.23.3
Local AS number : 103
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.1.1.1/32:
From: 10.1.23.2 (10.1.12.2)
Route Duration: 00h00m21s
Direct Out-interface: GigabitEthernet0/0/2
Original nexthop: 10.1.23.2
Qos information : 0x0
Community:<101:1>, no-export
AS-path 102 101, origin igp, pref-val 0, valid, external, best, select, active, pre 255
Not advertised to any peer yet
Check the route 10.1.1.1/32 on R3. The command output shows that the route carries two community values: 101:1 and no-export.
Overview
AS_Path Filter
Community Filter

## Slide 27: Configuring a Community Filter (1)
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
1. Configure a community filter to match the route carrying the community value 101:1.
Route filtering
2. Configure a matching rule that is based on the community filter.
3. Check the community filter information on R2.
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community=101:1
10.1.2.2/32 Community=101:2
R3
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
Route
10.1.2.2/32 Community=101:2
[R2] ip community-filter 1 permit 101:1
[R2] route-policy Community deny node 10
[R2-route-policy] if-match community-filter 1
[R2-route-policy] quit
[R2] route-policy Community permit node 20
[R2-route-policy] quit
[R2] bgp 102
[R2-bgp] peer 10.1.23.3 route-policy Community export
[R2]display ip community-filter 1
Community filter Number: 1
permit 101:1
Overview
AS_Path Filter
Community Filter

## Slide 28: Configuring a Community Filter (2)
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
4. Check the BGP routing information on R2.
Route filtering
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community=101:1
10.1.2.2/32 Community=101:2
R3
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
Route
10.1.2.2/32 Community=101:2
[R2]dis bgp routing-table 10.1.1.1
BGP local router ID : 10.1.12.2
Local AS number : 102
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.1.1.1/32:
From: 10.1.12.1 (10.1.1.1)
Route Duration: 00h13m39s
Direct Out-interface: GigabitEthernet0/0/1
Original nexthop: 10.1.12.1
Qos information : 0x0
Community:<101:1>
AS-path 101, origin igp, MED 0, pref-val 0, valid, external, best, select, active, pre 255
Not advertised to any peer yet
Check the route 10.1.1.1/32 on R2. The command output shows that the route carries the community value 101:1.
Use the community filter to filter out this route.
Overview
AS_Path Filter
Community Filter

## Slide 29: Configuring a Community Filter (3)
R2 transmits routes to the EBGP peer R3. Configure a routing policy on R2 to filter out the route carrying the community value 101:1.
5. Check the BGP routing table on R3.
Route filtering
AS 102
AS 103
AS 101
R1
10.1.1.1/32
10.1.2.2/32
R2
Route:
10.1.1.1/32 Community=101:1
10.1.2.2/32 Community=101:2
R3
10.1.12.0/24
.1
.2
.2
.3
10.1.23.0/24
Route
10.1.2.2/32 Community=101:2
[R3]display bgp routing-table
BGP Local router ID is 10.1.23.3
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.2.2/32 10.1.23.2 0 102 101i
R3 does not receive the BGP route 10.1.1.1/32.
Overview
AS_Path Filter
Community Filter

## Slide 30
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 31: On-Demand Route Advertisement by BGP Peers
If a device expects to receive only required routes from a remote device, and the remote device cannot maintain a separate outbound routing policy for each connected peer, you can configure a prefix-based outbound route filter (ORF) to implement on-demand route advertisement.
Route filtering
Prefix-based ORF enables a device to send locally configured prefix-based import policies to its BGP peers through Route-refresh messages. The BGP peers construct export policies based on the received policies (in Route-refresh messages) to filter routes to be advertised.
This prevents the local device from receiving a large number of unwanted routes, lowers the CPU usage of the local device, reduces the configuration workload on BGP peers, and lowers the link bandwidth usage.
ORF
Peer Group
Security
AS 101
10.1.1.1/32
10.1.2.2/32
R1
R2
AS 102
BGP route advertisement:
10.1.1.1/32
10.1.2.2/32
R2 filters routes on the inbound interface and accepts only the route 10.1.1.1/32.
For the routes that are filtered out (for example, route 10.1.2.2/32), actually R1 does not need to advertise them to R2.
4-Byte AS Number

## Slide 32: Basic ORF Configuration Commands
Configure a routing policy based on an IP prefix list to be associated with a specified peer or peer group.
Enable the prefix-based ORF capability on the local device for the peer or peer group.
Note: The ORF function must be enabled on both ends of a peer relationship.
[Huawei-bgp-af-ipv4] peer { group-name | ipv4-address } ip-prefix ip-prefix-name { import | export }
[Huawei-bgp] peer { group-name | ipv4-address } capability-advertise orf [ non-standard-compatible ] ip-prefix { both | receive | send } [ standard-match ]
ORF
Peer Group
Security
4-Byte AS Number
Notes: Command: [Huawei-bgp-af-ipv4] peer { group-name | ipv4-address } ip-prefix ip-prefix-name { import | export }
  import: applies the routing policy to the routes received from the peer or peer group.
  export: applies the routing policy to the routes to be advertised to the peer or peer group.
Command: [Huawei-bgp] peer { group-name | ipv4-address } capability-advertise orf [ non-standard-compatible ] ip-prefix { both | receive | send } [ standard-match ]
  non-standard-compatible: indicates that the ORF capability supported by the Huawei device is compatible with that supported by a non-Huawei device.
  both: enables the local device to both send and accept ORF packets.
  receive: enables the local device to only accept ORF packets.
  send: enables the local device to only advertise ORF packets.
  standard-match: matches routes according to the prefix matching rules defined in an RFC standard.

## Slide 33: Example for Configuring ORF
1. Configure a routing policy on R2 to filter the route 10.1.1.1/32, and enable ORF on R2 to allow R2 to send ORF packets.
R2 expects R1 to only advertise the route 10.1.1.1/32, and sends an ORF packet to R1 to meet this expectation.
2. Enable ORF on R1 to allow R1 to accept ORF packets.
[R2] ip ip-prefix 1 permit 10.1.1.1 32
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] peer 10.1.12.1 ip-prefix 1 import
[R2-bgp] peer 10.1.12.1 capability-advertise orf ip-prefix send
AS 101
AS 102
R1
R2
Route：
10.1.1.1/32
10.1.1.1/32
10.1.2.2/32
10.1.3.3/32
10.1.12.0/24
.1
.2
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] peer 10.1.12.2 capability-advertise orf ip-prefix receive
[R1-bgp] network 10.1.1.1 32
[R1-bgp] network 10.1.2.2 32
[R1-bgp] network 10.1.3.3 32
1
ORF
2
ORF
Peer Group
Security
4-Byte AS Number

## Slide 34: Verifying the ORF Configuration
1. On R1, check the prefix-based ORF information sent by R2.
2. Check the BGP routing information on R2.
Check the ORF information on R1. The command output shows that the route 10.1.1.1/32 is required.
Check the BGP routing information on R2. The command output shows that R2 has received only the route 10.1.1.1/32.
AS 101
AS 102
R1
R2
Route：
10.1.1.1/32
10.1.1.1/32
10.1.2.2/32
10.1.3.3/32
10.1.12.0/24
.1
.2
1
ORF
2
[R1]display bgp peer 10.1.12.2 orf ip-prefix
Total number of ip-prefix received: 1
Index Action Prefix MaskLen MinLen MaxLen
10 Permit 10.1.1.1 32
[R2]display bgp routing-table peer 10.1.12.1 received-routes
BGP Local router ID is 10.1.12.2
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 10.1.1.1/32 10.1.12.1 0 0 101i
ORF
Peer Group
Security
4-Byte AS Number

## Slide 35: BGP Peer Group
A peer group is a set of peers with the same policies. When a peer is added to a peer group, it inherits the configurations of the peer group. If the configurations of the peer group change, the configurations of all the peers in the group change accordingly.
A large number of BGP peers may exist on a large-scale BGP network, many of which need the same policies, you can configure a peer group to simplify configuration.
ORF
Peer Group
Security
4-Byte AS Number
Notes: Each peer in a peer group can be configured with its own policies for route advertisement and acceptance.

## Slide 36: Basic Peer Group Configuration Commands
Create a BGP peer group.
(Optional) Configure an AS number for the specified peer group.
A peer group is created in the BGP view, BGP-VPN instance IPv4 address family view, or BGP-VPN instance IPv6 address family view.
Add a specified peer to the peer group.
Specify the source interface for sending BGP messages and the source address for initiating a BGP connection.
An AS number is configured for the EBGP peer group. The AS number of an IBGP peer group is the local AS number of the device with the IBGP peer group configured.
[Huawei-bgp] group group-name [ external | internal ]
[Huawei-bgp] peer group-name as-number { as-number-plain | as-number-dot }
[Huawei-bgp] peer { ipv4-address | ipv6-address } group group-name
[Huawei-bgp] peer group-name connect-interface interface-type interface-number [ ipv4-source-address ]
ORF
Peer Group
Security
4-Byte AS Number
Notes: Command: [Huawei-bgp] group group-name [ external | internal ]
  group-name: specifies the name of a peer group. The value is a string of 1 to 47 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").
  external: creates an EBGP peer group.
  internal: creates an IBGP peer group.

## Slide 37: Example for Configuring a BGP Peer Group
1. Complete the basic BGP configuration on R1.
After R2 (ASBR) receives a route from its EBGP peer (R1), it advertises the route to all its IBGP peers (R3, R4, and R5). If R2 supports the BGP peer group function, it saves memory and improves route forwarding efficiency.
2. Complete the basic EBGP configuration and basic IBGP peer group configuration on R2.
Device | Interface | Interface Address | Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32 | R4 | Loopback0 | 10.1.4.4/32
R2 | Loopback0 | 10.1.2.2/32 | R5 | Loopback0 | 10.1.5.5/32
R3 | Loopback0 | 10.1.3.3/32 | / |  | 
3. Complete the basic IBGP configuration on R3.
The configurations of R4 and R5 are similar to the configuration of R3, and are not provided here.
AS 101
R2
R4
10.1.1.1/32
10.1.12.0/24
.1
.4
.2
R1
R3
R5
10.1.23.0/24
10.1.24.0/24
10.1.25.0/24
.2
.2
.2
.3
.5
AS 102
[R1] bgp 101
[R1-bgp] peer 10.1.12.2 as-number 102
[R1-bgp] network 10.1.1.1 32
[R2] bgp 102
[R2-bgp] peer 10.1.12.1 as-number 101
[R2-bgp] group in internal
[R2-bgp] peer 10.1.3.3 group in
[R2-bgp] peer 10.1.4.4 group in
[R2-bgp] peer 10.1.5.5 group in
[R2-bgp] peer in connect-interface Loopback 0
[R3] bgp 102
[R3-bgp] peer 10.1.2.2 as-number 102
[R3-bgp] peer 10.1.2.2 connect-interface Loopback 0
ORF
Peer Group
Security
4-Byte AS Number
Notes: As shown in the figure, assume that static routes are used or OSPF is used to ensure internal network reachability in AS 102. The configuration details are not provided here.

## Slide 38: Verifying the BGP Peer Group Configuration
1. Check the BGP peer group information on R2.
[R2]display bgp group in
BGP peer-group: in
Remote AS: 102
Authentication type configured: None
Type : internal
Configured hold timer value: 180
Keepalive timer value: 60
Connect-retry timer value: 32
Minimum route advertisement interval is 15 seconds
Connect-interface has been configured
PeerSession Members:
10.1.3.3 10.1.4.4 10.1.5.5
Peer Preferred Value: 0
No routing policy is configured
Peer Members:
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
10.1.3.3 4 102 5 7 0 00:03:33 Established 0
10.1.4.4 4 102 5 6 0 00:03:11 Established 0
10.1.5.5 4 102 4 6 0 00:02:52 Established 0
R2
R4
.4
.2
R3
R5
10.1.23.0/24
10.1.24.0/24
10.1.25.0/24
.2
.2
.2
.3
.5
AS 102
The command output shows that the peer group created on R2 is named in and has three IBGP peer members: 10.1.3.3, 10.1.4.4, and 10.1.5.5. All these members have established peer relationships with R2.
ORF
Peer Group
Security
4-Byte AS Number

## Slide 39: BGP Security
Common BGP attacks are as follows:
  A rogue BGP peer relationship is established, and invalid routes are advertised to disturb the normal routing table.
  A router receives a large number of bogus BGP messages and sends them to the CPU. As a result, the CPU usage goes excessively high.
BGP uses authentication and Generalized TTL Security Mechanism (GTSM) to ensure the security of message exchange between BGP peers.
Sends a large number of bogus BGP messages.
Rogue router
R1
Attacker
Establishes a rogue IBGP peer relationship and advertise the invalid Net1 route.
IBGP
AS 101
R2
IBGP
1
2
BGP Routing-table
*> Net1
The routing table of the authorized router is disturbed.
The CPU usage surges.
R3
ORF
Peer Group
Security
4-Byte AS Number

## Slide 40: BGP Authentication
BGP authentication is classified as MD5 authentication or keychain authentication. Authenticating BGP peer relationships can prevent rogue BGP peer relationships from being established.
BGP uses the Transmission Control Protocol (TCP) as its transport layer protocol. To enhance BGP security, MD5 authentication can be implemented when a TCP connection is established. You can set an MD5 authentication password for a TCP connection so that TCP implements MD5 authentication for BGP.
MD5 Authentication
R1
R2
TCP packets exchanged during the three-way handshake
Open messages
Update messages
Keepalive messages
Notification messages
The MD5 field in TCP packets is used for authentication.
Keychain is a set of key IDs. A key ID uniquely identifies authentication information, including the authentication password and algorithm.
You must configure keychain authentication for TCP-based applications on both BGP peers. Note that encryption algorithms and passwords configured for keychain authentication on both peers must be the same; otherwise, a TCP connection cannot be set up between BGP peers and BGP messages cannot be exchanged.
Keychain Authentication
R1
R2
When an application sends a packet, it uses the authentication information carried in a key ID to generate a message authentication code (MAC).
Fills the obtained MAC information
into the TCP Enhanced Authentication Option
After receiving the packet, the application uses the authentication information carried in the key ID to verify the MAC.
Returns a result (authentication success or failure)
BGP peer relationship
BGP peer relationship
ORF
Peer Group
Security
4-Byte AS Number
Notes: BGP uses TCP as its transport layer protocol and considers a TCP packet valid only if the source IP address, destination IP address, source port number, destination port number, and TCP sequence number in the packet are correct. Most of the preceding parameters in a TCP packet can be obtained by attackers without much difficulty. To protect BGP from attacks, use MD5 authentication or keychain authentication between BGP peers to reduce the possibility of attacks.
  The MD5 algorithm is easy to configure and generates a single password, which can only be manually changed.
  The keychain algorithm is complex to configure and generates a set of passwords. Keychain authentication allows passwords to be changed automatically based on configurations. Therefore, keychain authentication is applicable to networks requiring high security.
Note: BGP MD5 authentication and BGP keychain authentication are mutually exclusive.

## Slide 41: BGP GTSM
BGP GTSM can check whether the time to live (TTL) value in the IP packet header is within a preset range, and drop the packets whose TTL values are not within the preset range. This prevents bogus BGP messages from attacking the device.
When an attacker continuously sends bogus BGP messages to attack R2, the TTL values of such messages are smaller than 255.
If BGP GTSM is enabled on R2 and the valid TTL range for messages sent by the IBGP peer is set to [255, 255], the system checks the TTL values of all BGP messages and drops the bogus messages whose TTL values are smaller than 255. This prevents the bogus messages from consuming CPU resources.
Sends a large number of bogus BGP messages.
GTSM is deployed, and the minimum TTL value of the BGP messages to be accepted is set to 255.
The bogus BGP messages have excessively small TTL values after reaching R2 and are therefore dropped.
R1
R2
Attacker
IBGP
AS101
ORF
Peer Group
Security
4-Byte AS Number
Notes: As shown in the figure, if BGP GTSM is not enabled, the device finds that the received numerous bogus BGP messages are destined for itself, and directly sends them to the control plane for processing. As a result, the control plane has to process a large number of bogus messages, causing the CPU usage to go excessively high and the system to be unexpectedly busy.

## Slide 42: Basic BGP Authentication Configuration Commands
Configure MD5 authentication for BGP messages exchanged during the establishment of a TCP connection with a specified peer or peer group.
Configure keychain authentication for the establishment of a TCP connection with a specified peer or peer group.
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } password { cipher cipher-password | simple simple-password }
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } keychain keychain-name
ORF
Peer Group
Security
4-Byte AS Number
Notes: Command: [Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } keychain keychain-name
  keychain-name: specifies the name of a keychain. The value is a string of 1 to 47 case-insensitive characters. It cannot contain question marks (?). If spaces are used, the string must start and end with double quotation marks (").

## Slide 43: Basic GTSM Configuration Commands
Apply the GTSM function to a BGP peer or peer group.
(Optional) Set a default action to take on messages that do not match the GTSM policy.
(Optional) Enable the logging function on all boards to record log information when GTSM discards messages.
By default, no log information is recorded on any board when GTSM drops messages.
You can run this command to enable the logging function so that the device can record information about the messages dropped by GTSM in logs. The recorded logs facilitate fault locating.
By default, the messages that do not match a GTSM policy can pass filtering.
GTSM configurations are symmetrical. That is, you need to enable GTSM on both ends of a BGP peer relationship.
[Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } valid-ttl-hops [ hops ]
[Huawei] gtsm default-action { drop | pass }
[Huawei] gtsm log drop-packet all
ORF
Peer Group
Security
4-Byte AS Number
Notes: Command: [Huawei-bgp] peer { group-name | ipv4-address | ipv6-address } valid-ttl-hops [ hops ]
  hops: specifies the number of TTL hops to be checked. The value is an integer ranging from 1 to 255. The default value is 255. If you specify hops, the valid range of TTL values in the messages to be checked is [255 – hops + 1, 255].
Command: [Huawei] gtsm default-action { drop | pass }
  drop: indicates that the messages that do not match the GTSM policy cannot pass filtering and are dropped.
  pass: indicates that the messages that do not match the GTSM policy can pass filtering.
Command: [Huawei] gtsm log drop-packet all
  all: indicates all boards.

## Slide 44: Example for Configuring GTSM (1)
1. Establish full-mesh IBGP connections.
R1, R2, and R3 all belong to AS 101 and use loopback0 interfaces to establish full-mesh IBGP connections. GTSM needs to be enabled on them to prevent CPU attacks.
Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32
R2 | Loopback0 | 10.1.2.2/32
R3 | Loopback0 | 10.1.3.3/32
R1
R2
.2
R3
10.1.12.0/24
10.1.23.0/24
.1
AS 101
.2
.3
IBGP peer relationship
IBGP peer relationship
IBGP peer relationship
[R1] bgp 101
[R1-bgp] peer 10.1.2.2 as-number 101
[R1-bgp] peer 10.1.2.2 connect-interface Loopback 0
[R1-bgp] peer 10.1.3.3 as-number 101
[R1-bgp] peer 10.1.3.3 connect-interface Loopback 0
[R1-bgp] network 10.1.1.1 32
[R2] bgp 101
[R2-bgp] peer 10.1.1.1 as-number 101
[R2-bgp] peer 10.1.1.1 connect-interface Loopback 0
[R2-bgp] peer 10.1.3.3 as-number 101
[R2-bgp] peer 10.1.3.3 connect-interface Loopback 0
[R3] bgp 101
[R3-bgp] peer 10.1.1.1 as-number 101
[R3-bgp] peer 10.1.1.1 connect-interface Loopback 0
[R3-bgp] peer 10.1.2.2 as-number 101
[R3-bgp] peer 10.1.2.2 connect-interface Loopback 0
ORF
Peer Group
Security
4-Byte AS Number
Notes: As shown in the figure:
  Assume that static routes are used or OSPF is used to ensure internal network reachability in AS 101. The configuration details are not provided here.
  R1 advertises the route destined for the IP address of its loopback0 interface to the BGP routing table.

## Slide 45: Example for Configuring GTSM (2)
R1, R2, and R3 all belong to AS 101 and use loopback0 interfaces to establish full-mesh IBGP connections. GTSM needs to be enabled on them to prevent CPU attacks.
Device | Interface | Interface Address
R1 | Loopback0 | 10.1.1.1/32
R2 | Loopback0 | 10.1.2.2/32
R3 | Loopback0 | 10.1.3.3/32
R1
R2
.2
R3
10.1.12.0/24
10.1.23.0/24
.1
AS 101
.2
.3
IBGP peer relationship
IBGP peer relationship
IBGP peer relationship
2. Enable GTSM between R1 and R2. As the two routers are directly connected, the valid TTL range of the messages from one router to the other is [255, 255]. In this case, the value of valid-ttl-hops is 1.
3. Enable GTSM between R2 and R3. As the two routers are directly connected, the valid TTL range of the messages from one router to the other is [255, 255]. In this case, the value of valid-ttl-hops is 1.
4. Enable GTSM between R1 and R3. As the two routers are connected through R2, the valid TTL range of the messages from one end to the other is [254, 255]. In this case, the value of valid-ttl-hops is 2.
[R1-bgp] peer 10.1.2.2 valid-ttl-hops 1
[R2-bgp] peer 10.1.1.1 valid-ttl-hops 1
[R2-bgp] peer 10.1.3.3 valid-ttl-hops 1
[R3-bgp] peer 10.1.2.2 valid-ttl-hops 1
[R1-bgp] peer 10.1.3.3 valid-ttl-hops 2
[R3-bgp] peer 10.1.1.1 valid-ttl-hops 2
ORF
Peer Group
Security
4-Byte AS Number

## Slide 46: Verifying the GTSM Configuration
Run the display bgp peer command to check BGP peer information.
By specifying the verbose parameter, you can check information about the BGP timer, numbers of received and sent routes, capabilities supported by the peer, and enabled functions.
[R1]display bgp peer 10.1.3.3 verbose
BGP Peer is 10.1.3.3, remote AS 101
Type: IBGP link
BGP version 4, Remote router ID 10.1.3.3
Update-group ID: 1
BGP current state: Established, Up for 00h02m17s
BGP current event: KATimerExpired
BGP last state: OpenConfirm
BGP Peer Up count: 1
Received total routes: 0
Received active routes total: 0
Advertised total routes: 1
Port: Local - 179 Remote - 51077
Configured: Connect-retry Time: 32 sec
Configured: Active Hold Time: 180 sec Keepalive Time:60 sec
Received : Active Hold Time: 180 sec
Negotiated: Active Hold Time: 180 sec Keepalive Time:60 sec
Peer optional capabilities:
Peer supports bgp multi-protocol extension
Peer supports bgp route refresh capability
Peer supports bgp 4-byte-as capability
Received: Total 5 messages
Update messages 0
Open messages 1
KeepAlive messages 3
Notification messages 0
Refresh messages 1
Sent: Total 8 messages
Update messages 2
Open messages 2
KeepAlive messages 3
Notification messages 0
Refresh messages 1
Authentication type configured: None
Last keepalive received: yy/mm/dd 17:34:13 UTC-08:00
Last keepalive sent : yy/mm/dd 17:34:13 UTC-08:00
Last update sent : yy/mm/dd 17:34:02 UTC-08:00
Minimum route advertisement interval is 15 seconds
Optional capabilities:
Route refresh capability has been enabled
4-byte-as capability has been enabled
Connect-interface has been configured
GTSM has been enabled, valid-ttl-hops: 2
Peer Preferred Value: 0
Routing policy configured:
No routing policy is configured
To be continued on the right
GTSM is enabled on R1, and the number of valid hops between R1 and its IBGP peer 10.1.3.3 (R3) is 2.
ORF
Peer Group
Security
4-Byte AS Number

## Slide 47: 4-Byte AS Number
As networks expand, allocatable AS numbers are about to be exhausted.
Currently, AS numbers used on networks range from 1 to 65535 (2-byte AS number range). The AS number range needs to be extended to 1 to 4294967295 (4-byte AS number range). BGP devices that support 4-byte AS numbers are compatible with BGP devices that support only 2-byte AS numbers.
Speaker: Each router that sends BGP messages is called a BGP speaker. It receives or generates new routing information and advertises the information to other BGP speakers.
Peer: BGP speakers that exchange messages with each other are called peers.
New speaker: a BGP peer that supports 4-byte AS numbers.
Old speaker: a BGP peer that does not support 4-byte AS numbers.
New session: a BGP connection established between new speakers.
Old session: a BGP connection established either between a new speaker and an old speaker or between old speakers.
Related Concepts
A 4-byte AS number can be either an integer or in dotted notation. 4-byte AS numbers are stored as unsigned integers, regardless of their formats.
4-byte AS numbers in dotted notation are in the format of x.y.
The formula for the conversion between a 4-byte AS number in integer format and a 4-byte AS number in dotted format is as follows: 4-byte AS number in integer format = x x 65536 + y.
For example, the 4-byte AS number (2.3) in dotted notation can be converted through the formula (2 x 65536 + 3) to the 4-byte AS number (131075) in integer format.
Formats of 4-byte AS Numbers
ORF
Peer Group
Security
4-Byte AS Number
Notes: 4-byte AS numbers are extended from 2-byte AS numbers. BGP peers use a new capability code and new optional transitive attributes to negotiate the 4-byte AS number capability and transmit 4-byte AS numbers. This mechanism enables communication between new speakers as well as between old speakers and new speakers.
  To support 4-byte AS numbers, an open capability code 0x41 is defined in a standard protocol for BGP connection capability negotiation. 0x41 indicates that the BGP speaker supports 4-byte AS numbers.
  In addition, two new optional transitive attributes AS4_Path and AS4_Aggregator are defined in the standard protocol to transmit 4-byte AS information in old sessions.
  To set up a BGP connection between a new speaker with an AS number greater than 65535 and an old speaker, the peer AS number on the old speaker must be set to AS_TRANS, which is a reserved AS number with the value being 23456.
NetEngine 8000 series routers support configuration of 4-byte AS numbers in either format. The formats of 4-byte AS numbers displayed in the configuration file are the same as those used by users during configuration.

## Slide 48: Open Messages Carrying 4-Byte AS Numbers
BGP speakers negotiate capabilities by exchanging Open messages. The format of Open messages sent by new speakers is shown in the figure at the bottom of this slide.
Open message:
Old Speaker
New Speaker
Version |  | 
My AS Number |  | 
Hold Time |  | 
BGP Identifier |  | 
Length |  | 
Optional parameters |  | 
AS_TRANS
23456
4-byte AS number
Open messages are exchanged to negotiate the 4-byte AS number capability.
The header of a BGP Open message is fixed, in which My AS Number is supposed to be the local AS number. However, My AS Number has only 2 bytes, unable to support 4-byte AS numbers.
Therefore, a new speaker places the AS_TRANS 23456 in My AS Number and its AS number in Optional parameters before it sends an Open message to a peer. After the peer receives the message, it can determine whether the other end supports 4-byte AS numbers by checking Optional parameters in the message.
AS 65001
AS 1.1
ORF
Peer Group
Security
4-Byte AS Number

## Slide 49: Fundamentals of 4-Byte AS Numbers
The following figure shows the process of establishing peer relationships and transmitting routing information between new speakers and between new speakers and old speakers.
Old Speaker
New Speaker
AS 65001
AS 1.1
New Speaker
AS 2.2
I have the 4-byte AS number capability.
I have the 4-byte AS number capability.
I do not have the 4-byte AS number capability.
I have the 4-byte AS number capability too.
Old session
New session
Routes carrying AS_Path and AS4_Path attributes
Routes carrying the AS_Path attribute
Routes carrying the AS_Path attribute
Routes carrying the AS_Path attribute
Open messages
4-byte AS number capability negotiation
Update messages
Routing information transfer
Peer relationship establishment
BGP speakers notify each other of whether they have the 4-byte AS number capability by exchanging Open messages. After the capability negotiation, new sessions are established between new speakers, and old sessions are established between a new speaker and an old speaker.
ORF
Peer Group
Security
4-Byte AS Number
Notes: Note: When transmitting routing information to an old speaker, a new speaker encapsulates both the AS_Path and AS4_Path attributes to help transmit 4-byte AS numbers. The AS4_Path attribute is transitive. Therefore, when the old speaker receives the AS4_Path attribute, it transmits the AS4_Path attribute to other speakers.

## Slide 50: Transmission of 4-Byte AS Numbers
In the Update messages exchanged between new speakers, AS numbers in the AS_Path attribute are encoded in 4-byte mode. In the Update messages sent by old speakers, AS numbers in the AS_Path attribute are encoded in 2-byte mode.
Old speaker
New speaker
AS 65001
AS 1.1
New speaker
AS 2.2
Old speaker
AS 65002
New speaker
AS 65003
AS_Path
(65001)
(1.1, 65001)
(23456, 23456, 65001)
(65002, 2.2, 1.1, 65001)
(65001)
(1.1, 65001)
(23456, 23456, 65001)
(65002, 23456, 23456, 65001)
(2.2, 1.1, 65001)
(2.2, 1.1, 65001)
AS_Path in Update messages
AS4_Path in Update messages
ORF
Peer Group
Security
4-Byte AS Number
Notes: When a new speaker sends an Update message carrying an AS number greater than 65535 to an old speaker, the new speaker uses the AS4_Path attribute to assist the AS_Path attribute in transferring 4-byte AS numbers. The AS4_Path attribute is transparent to the old speaker.
  On the network shown in this figure, before the new speaker in AS 2.2 sends an Update message to the old speaker in AS 65002, the new speaker replaces each 4-byte AS number (1.1 and 2.2) with 23456 (AS_TRANS) in AS_Path; therefore, the AS_Path carried in the Update message is (23456, 23456, 65001), and the carried AS4_Path is (2.2, 1.1, 65001). Upon receiving the Update message, the old speaker in AS 65002 transparently transmits AS4_Path (2.2, 1.1, 65001) to another AS.
When a new speaker receives an Update message carrying the AS_Path and AS4_Path attributes from an old speaker, the new speaker obtains the actual AS_Path attribute based on the reconstruction algorithm.
  In the figure, after the new speaker in AS 65003 receives an Update message carrying AS_Path (65002, 23456, 23456, 65001) and AS4_Path (2.2, 1.1, 65001) from the old speaker in AS 65002, the new speaker obtains the actual AS_Path (65002, 2.2, 1.1, 65001) through reconstruction.

## Slide 51: 4-Byte AS Number Configuration
Configuration example:
  R1 and R2 are in AS 1.1 and use Loopback0 interfaces to establish an IBGP peer relationship.
[Huawei] bgp as-number
Enable BGP and enter the BGP view, or directly enter the BGP view.
as-number: specifies an AS number.
For an AS number in integer format, the value ranges from 1 to 4294967295.
For an AS number in dotted notation, it is in the format of x.y, in which x and y are integers, with x ranging from 1 to 65535 and y ranging from 0 to 65535.
R1
R2
.2
10.1.12.0/24
.1
AS 1.1
IBGP peer
[R1] bgp 1.1
[R1-bgp] peer 10.1.2.2 as-number 1.1
[R1-bgp] peer 10.1.2.2 connect-interface Loopback 0
Establish an IBGP connection.
[R2] bgp 1.1
[R2-bgp] peer 10.1.1.1 as-number 1.1
[R2-bgp] peer 10.1.1.1 connect-interface Loopback 0
Loopback0
10.1.1.1
Loopback0
10.1.2.2
ORF
Peer Group
Security
4-Byte AS Number
Notes: In the figure:
  Assume that static routes are configured or OSPF is used to ensure internal network reachability in AS 1.1. The configuration details are not provided here.
  Configure R1 to advertise the route to Loopback0's address to BGP. The configuration details are not provided here.
Notes:
  This slide uses NetEngine 8000 series routers as an example. For the 4-byte AS number configuration on any other type of product, see the corresponding product documentation.
  If you adjust the display format of 4-byte AS numbers, the matching results in the case of filtering using AS_Path regular expressions or extended community filters are affected. Specifically, after the display format of 4-byte AS numbers is changed when an AS_Path regular expression or extended community filter has been used in an export or import policy, the AS_Path regular expression or extended community filter needs to be reconfigured. If reconfiguration is not performed, routes may fail to match the export or import policy, leading to a network fault.

## Slide 52
BGP Route Control
Introduction to BGP Features
Networking Modes of BGP RRs

## Slide 53: RR
Using RRs can avoid the need for full-mesh IBGP connections and reduce the burden on the network and CPU.
After an RR is introduced, three roles exist:
  Route reflector
  Client
  Non-client
The RR reflects the learned routes so that IBGP routes are advertised in the AS, avoiding the need to establish full-mesh IBGP connections.
After the RR receives routes from its peers, it selects the optimal route based on BGP route selection rules and advertises the optimal route to IBGP peers based on certain rules.
AS 103
R5
OSPF
AS 101
RR
R3
R2
IBGP
AS 102
R4
10.1.1.1/32
IBGP
BGP Update message
R1
Client
Non-Client
EBGP
EBGP
Notes: RR-related roles:
  RR: BGP device that reflects the routes learned from an IBGP peer to other IBGP peers. An RR is similar to the designated router (DR) on an OSPF network.
  Client: IBGP peer whose routes are reflected by the RR to other IBGP peers. In an AS, clients only need to be directly connected to the RR.
  Non-client: IBGP device that is neither an RR nor a client. In an AS, full-mesh connections still must be established between non-clients and RRs, and between all non-clients.
  Originator: device that originates routes in an AS. The Originator_ID attribute is used to prevent routing loops in a cluster.
  Cluster: a set of RRs and their clients. The Cluster_List attribute is used to prevent routing loops between clusters.
When configuring a BGP router as an RR, you also need to specify a client of the RR. A client does not need to be configured because it is not aware that an RR exists on the network.
Rules for an RR to advertise routes:
  After learning routes from non-clients, the RR selects and advertises the optimal route to all its clients.
  After learning routes from clients, the RR selects and advertises the optimal route to all its non-clients and clients (except the originating client).
  After learning routes learned from EBGP peers, the RR selects and advertises the optimal route to all its clients and non-clients.

## Slide 54: Backup RR Networking
To improve network reliability and prevent a single point of failure (SPOF) from affecting the network, multiple RRs need to be configured in a cluster. Routers on a forwarding path establish IBGP peer relationships with all RRs. Any of the RRs has complete BGP routes.
RR1 and RR2 are in the same cluster and configured with the same cluster ID.
Route reflection in single-cluster RR networking (RR1 is used as an example):
  When client 1 receives an updated route from an EBGP peer, it advertises this route to RR1 and RR2 through IBGP peer relationships.
  After RR1 and RR2 receive this route, they add the local cluster ID to the top of the cluster list of the route, and then reflect the route to client 2 and to each other.
  After RR1 and RR2 receive the reflected route, they check the cluster list of the route, finding that the cluster list contains their local cluster ID. RR1 and RR2 discard this route to reduce BGP memory usage.
IBGP peer relationship
BGP Update message
RR1
RR2
Client1
Client2
AS 101
Cluster
IBGP
IBGP
IBGP
R1
AS 102
EBGP
10.1.1.1/32
1
2
3

## Slide 55: Multi-cluster RR Networking (1)
If multiple clusters exist in an AS, RRs of the clusters establish IBGP peer relationships with each other.
When RRs reside at the same network layer, RRs of different clusters can establish full-mesh connections to implement flat RR.
An AS on a backbone network may be divided into multiple clusters. RRs of the clusters are non-clients of each other and establish full-mesh IBGP connections with each other.
Although each client in a cluster establishes an IBGP connection only with the RR in the same cluster, each RR and client can receive all the routing information.
As shown in the figure, one RR resides in each cluster: 1, 2, 3, and 4. An IBGP connection is established between any two of the RRs. Each client in a cluster establishes an IBGP connection only with the RR in the same cluster.
IBGP peer relationship
RR
Client1
AS 101
IBGP
Cluster1
Cluster3
Cluster4
Cluster2
RR
RR
RR
Client2
Client1
Client2
Client
Client

## Slide 56: Multi-cluster RR Networking (2)
If multiple clusters exist in an AS, RRs of the clusters establish IBGP peer relationships with each other.
When the RRs reside at different network layers, the RRs at the lower network layer can be configured as clients to implement hierarchical RR.
In practice, hierarchical RR deployment is used more widely.
As shown in the figure, AS 101 is divided into three clusters:
  The four devices in cluster 1 are core routers and work in master/backup mode to ensure high reliability. Two Level-1 RRs are deployed in cluster 1, and the other two routers function as clients of the RRs.
  A Level-2 RR is deployed in each of cluster 2 and cluster 3. The Level-2 RRs are also clients of the Level-1 RRs. An IBGP connection does not need to be established between the Level-2 RRs.
Client
Level-1 RR1
Client1/
Level-2 RR
AS 101
Cluster1
IBGP
IBGP
IBGP
Client
Client2/
Level-2 RR
Cluster2
Cluster3
Level-1 reflection
IBGP peer relationship
Level-1 RR2
Level-2 reflection
Notes: The route advertisement rules for hierarchical RR networking are the same as those for single-cluster RR networking.
The following factors need to be considered for hierarchical RR design:
  Size of the top-layer full-mesh topology: If the number of full-mesh IBGP connections has exceeded the management capacity, hierarchical RR networking can be deployed.
  Number of alternate paths: This factor affects load balancing and resource consumption. More layers reduce the number of links for load balancing but require fewer router resources.

## Slide 57: Single-Cluster Problem
To provide the desired redundancy in an RR-based architecture, it is important to properly divide an AS into clusters.
Scenario description:
  As shown in the figure, AS 101 uses the backup RR networking. RR1 and RR2 use the same cluster ID, and provide a redundant link for traffic from R1 to access 10.1.5.5/32.
  After R4 advertises the route 10.1.5.5/32, the two RRs advertise the route to R1 and to each other. Because RR1 and RR2 have the same cluster ID, the Update messages exchanged between the RRs are discarded.
An IBGP session failure causes the redundancy failure:
  Assume that the IBGP session between R3 and R4 fails (for example, due to incorrect configurations). As R3 ignores the route 10.1.5.5/32 advertised by R2, no redundant link is available for traffic from R1 to access 10.1.5.5/32.
AS 101
AS 102
R1
Route:
10.1.5.5/32
10.1.5.5/32
R2
R3
R4
R5
Cluster
RR1
RR2
Client

## Slide 58: Multi-cluster Design
Multi-cluster design not only provides physical redundancy in response to link failures, but also provides logical redundancy in response to IBGP session failures between clients and RRs.
As shown in the figure, R2 and R4 are added to cluster 1, and R3 and R4 are added to cluster 2.
If the IBGP session between R3 and R4 fails, R3 can still forward traffic because R3 learns the route 10.1.5.5/32 advertised by R2.
AS 101
AS 102
R1
Route:
10.1.5.5/32
10.1.5.5/32
R2
R3
R4
R5
Cluster1
RR1
RR2
Client
Cluster2

## Slide 59
(Single-answer question) Which of the following AS_Path value is matched against the ip as-path-filter 1 permit ^[100|200]$ command? ( )
  AS_Path 100
  AS_Path 200
  AS_Path 100 200
  AS_Path 100 or AS_Path 200
Notes: D

## Slide 60
(True or false) Authenticate BGP peer relationships can prevent unauthorized BGP peer relationships from being established. ( )
  True
  False
(True or false) In the backup RR networking of BGP, the master and backup RRs discard the routes reflected by each other to prevent routing loops. ( )
  True
  False
Notes: A
A

## Slide 61
As dedicated route matching tools of BGP, AS_Path and community filters can be used to match BGP routes based on the AS_Path and community attributes, respectively, and can be used with route-policies to implement BGP route control.
BGP also supports various advanced features, including ORF to achieve on-demand route advertisement, peer groups to simplify configurations, BGP security features to prevent the establishment of rogue peer relationships as well as attacks through bogus BGP messages, and 4-byte AS numbers to meet future network expansion requirements.
BGP uses RRs to break the split horizon rule of IBGP, avoid the need for full-mesh IBGP connections, and reduce the burden on the network and CPU. Common RR networking modes include backup-RR networking and multi-cluster RR networking.