## Slide 1
Datacom
General
V1.0
He Junjian/WX580230
2020.08.10
Wu Yue/WX291773
New

## Slide 2: Inter-AS MPLS L3VPN

## Slide 3
As the MPLS VPN solution has been widely adopted, the user quantity and network scale are increasing rapidly, and the number of sites in an enterprise keeps increasing. Sites in different geographical locations or autonomous systems (ASs) need to be interconnected across ASs.
To support the exchange of VPN routing information between ASs, the existing protocol needs to be extended and the MPLS VPN architecture needs to be modified to provide an interconnection model different from the basic MPLS VPN architecture, that is, the inter-AS MPLS VPN.
RFC4364 proposed three inter-AS VPN solutions: inter-AS VPN Option A, inter-AS VPN Option B, and inter-AS VPN Option C.
This document describes the fundamentals and configurations of the three inter-AS MPLS VPN solutions.

## Slide 4
On completion of this course, you will be able to:
  Describe the fundamentals of the three inter-AS VPN solutions.
  Perform basic configurations of the three inter-AS VPN solutions.
  Illustrate the application scenarios of the three inter-AS VPN solutions.

## Slide 5
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
Fundamentals and Configurations of Inter-AS VPN Option B
Fundamentals and Configurations of Inter-AS VPN Option C

## Slide 6: Fundamentals of Intra-AS MPLS VPN: Route Advertisement and Label Distribution
FEC: PE1
Label: T2
FEC: PE1
Label: T1
CE1
CE2
Site1
MP-IBGP
2
Site2
IGP/BGP
1
LDP
4
IGP/BGP
3
LDP
4
MPLS backbone network
IPv4: Net1
NH: CE1
VPNv4: RD1+Net1
NH: PE1
VPN Label: V1
IPv4: Net1
NH: PE2
IPv4 routing
VPNv4 routing
IPv4 routing
The following example describes how CE1 advertises routes to CE2.
CE1 and PE1 run IGP/BGP to exchange routing information (IPv4 routes).
After PE1 receives a route from CE1, PE1 converts the route into a VPNv4 route, advertises the VPNv4 route to PE2 using MP-IBGP, and allocates a VPN label V1 to the route.
After PE2 receives the VPNv4 route, PE2 converts the route into an IPv4 route and advertises the route to CE2 using IGP/BGP.
PEs and the P on the MPLS backbone network run LDP to allocate tunnel labels. Assume that the labels allocated by PE1 and allocated by P to PE1 are T1 and T2 respectively.
Only PEs are aware of VPN routing information, while the P device is not.
The backbone network uses MPLS tunnel forwarding to avoid routing blackholes.
P
PE2
PE1

## Slide 7: Fundamentals of Intra-AS MPLS VPN: Data Forwarding
P
PE2
PE1
CE1
CE2
Site1
Site2
MPLS backbone network
The following example describes how CE2 sends a data packet to CE1.
CE2 sends an IPv4 packet with the destination address Net1.
After PE2 receives the packet, it encapsulates the packet with a VPN label V1 and then an outer label T2 and forwards the packet to the P device.
The P device swaps the outer label T2 with T1 and forwards the packet to PE1.
PE1 removes all labels from the packet and forwards the packet to CE1.
IP
Net1
Net1
V1
T2
MPLS
Net1
V2
T1
MPLS
IP
Net1
1
2
3
4
IPv4
VPN
LDP LSP

## Slide 8: Background of Inter-AS MPLS VPN Solutions
As the enterprise scale keeps increasing, enterprise sites in different locations may belong to different ASs. As shown in the figure, when CEs in two different ASs need to communicate with each other, the inter-AS VPN technology is required.
P
PE2
PE1
CE1
CE3
AS100
P
PE2
PE1
CE4
CE2
P1
ASBR-PE1
PE1
CE1
CE3
P2
PE2
ASBR-PE2
CE4
CE2
EBGP or static routing
Devices in ASs communicate using EBGP or static routing.
AS200
AS100
AS200
Notes: To facilitate understanding, the devices connecting ASs in the original AS are called ASBR-PEs, and P devices are numbered differently. In addition, CE3 and CE4 will not be discussed.

## Slide 9: Problems Caused by Inter-AS MPLS VPN
Compared with intra-AS MPLS VPN, inter-AS MPLS VPN has similar fundamentals but faces the following problems:
  LDP does not run between ASs, as a result of which, outer tunnels cannot be established between ASs.
  PEs do not run IGP, cannot establish BGP peer relationships between each other by default, and so cannot directly advertise VPNv4 routes to each other.
The solutions to the preceding problems are as follows:
  ASBRs exchange IPv4 routes and forward IPv4 data packets. This solution is easy to understand.
  ASBRs exchange VPNv4 routes and forward packets carrying one MPLS label.
  PEs exchange VPNv4 routes and forward packets carrying multiple MPLS labels.
P1
ASBR-PE1
PE1
CE1
AS100
P2
PE2
ASBR-PE2
CE2
AS200
New backbone network
Option A
Option B
Option C

## Slide 10: Inter-AS MPLS VPN Solutions
The following describes three inter-AS MPLS VPN solutions:
  Inter-Provider Backbones Option A (inter-AS VPN Option A)
    VPN instances spanning multiple ASs are bound to dedicated interfaces of ASBRs to manage their own VPN routes. This solution is also called VRF-to-VRF.
    The configuration is simple, without requiring MPLS to run between ASBRs.
  Inter-Provider Backbones Option B (inter-AS VPN Option B)
    ASBRs advertise labeled VPNv4 routes to each other using MP-EBGP. This solution is also called EBGP redistribution of labeled VPNv4 routes.
    With this solution, you do not need to create a different interface for each VPN.
  Inter-Provider Backbones Option C (inter-AS VPN Option C)
    PEs or route reflectors (RRs) advertise labeled VPNv4 routes to each other using multi-hop MP-EBGP. This solution is also called multi-hop EBGP redistribution of labeled VPNv4 routes.
    The configuration is complex because ASBRs do not maintain or advertise VPNv4 routes.

## Slide 11
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
  Fundamentals
  Basic Configurations
Fundamentals and Configurations of Inter-AS VPN Option B
Fundamentals and Configurations of Inter-AS VPN Option C

## Slide 12: Inter-AS VPN Option A Overview
As a basic BGP/MPLS IP VPN application in the inter-AS scenario, Option A does not need special configurations and MPLS does not need to run between ASBRs. In this mode, ASBRs of two ASs directly connect to each other and function as PEs in the ASs. Each ASBR views the peer ASBR as its CE and advertises IPv4 routes to the peer ASBR using EBGP.
P1
ASBR-PE1
PE1
CE1
AS100
P2
PE2
ASBR-PE2
CE2
AS200
P1
ASBR-PE1
PE1
CE1
CE2
ASBR-PE2
P2
PE2
ASBR-PE2
CE1
CE2
ASBR-PE1 views ASBR-PE2 as its CE.
ASBR-PE2 views ASBR-PE1 as its CE.
ASBR-PE1
Each VPN instance uses a different logical link.
ASBRs exchange IPv4 routes.
EBGP
EBGP
EBGP
AS100
AS200

## Slide 13: Inter-AS VPN Option A Topology
Two ASBR-PEs are connected through multiple physical interfaces (or sub-interfaces), each interface is bound to a VPN, and each ASBR-PE views the peer ASBR-PE as a CE. Therefore, the interfaces connecting the two ASBR-PEs need to be bound to VRFs, and VPNv4 routes need to be converted into common IPv4 routes using EBGP and transmitted from one AS to another AS. Therefore, the two ASBRs need to be interconnected, but MPLS does not need to be enabled.
PE1
PE2
ASBR-PE1
ASBR-PE2
P1
P2
CE1
CE2
IP/MPLS
MP-IBGP
IP/MPLS
MP-IBGP
AS100
AS200
EBGP
IPv4
VPN
LDP LSP

## Slide 14: Inter-AS VPN Option A: Control Plane
CE1 sets the next hop of an IPv4 route to itself and advertises the route to PE1.
PE1 converts the IPv4 route into a VPNv4 route, sets the next hop of the route to PE1, allocates a VPN label V1 to the route, and advertises the route to ASBR-PE1.
PE1 and P1 allocate tunnel labels T1 and T2 respectively to the routes destined for PE1.
ASBR-PE1 converts the VPNv4 route into an IPv4 route, sets the next hop to ASBR-PE1, and advertises the route to ASBR-PE2.
ASBR-PE2 converts the IPv4 route into a VPNv4 route, sets the next hop of the route to ASBR-PE2, allocates a VPN label V2 to the route, and advertises the route to PE2.
ASBR-PE2 and P2 allocate tunnel labels T3 and T4 respectively to the routes destined for ASBR-PE2.
PE2 converts the VPNv4 route into an IPv4 route, sets the next hop to PE2, and advertises the route to CE2.
IPv4 routing
Tunnel label
Tunnel label
IPv4 routing
VPNv4 routing
IPv4 routing
Tunnel label
Tunnel label
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
FEC: PE1
Label: T1
FEC: PE1
Label: T2
VPNv4: RD1+Net1
NH: PE1
VPN label: V1
IPv4: Net1
NH: CE1
IPv4: Net1
NH: ASBR-PE1
FEC: ASBR-PE2
Label: T3
FEC: ASBR-PE2
Label: T4
VPNv4 routing
VPNv4: RD2+Net1
NH: ASBR-PE2
VPN label: V2
IPv4: Net1
NH: PE2
Net1
IP/MPLS
MP-IBGP
IP/MPLS
MP-IBGP
P1
P2
AS100
AS200
The following example describes how CE1 advertises a route to CE2.
1
2
4
5
7
3
3
6
6
Notes: The numbers in this example are only for ease of understanding, and do not represent the actual processing sequence on the devices.

## Slide 15: Inter-AS VPN Option A: Forwarding Plane
CE2 sends an IP packet destined for Net1 to PE2.
After PE2 receives the IP packet, it encapsulates the packet with a VPN label V2 and then an outer label T4 and forwards the packet to P2.
P2 swaps the outer label T4 with T3 and forwards the packet to ASBR-PE2.
ASBR-PE2 removes all labels from the packet and forwards the packet to ASBR-PE1.
After ASBR-PE1 receives the IP packet, it encapsulates the packet with a VPN label V1 and then an outer label T2 and forwards the packet to P1.
P1 swaps the outer label T2 with T1 and forwards the packet to PE1.
PE1 removes all labels from the packet and forwards the packet to CE1.
IP
MPLS
MPLS
MPLS
MPLS
IP
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
Site1
Site2
Net1
Net1
IP/MPLS
MP-IBGP
IP/MPLS
MP-IBGP
Net1
V2
T4
Net1
V2
T3
IP
Net1
Net1
V1
T2
Net1
V1
T1
Net1
P1
P2
AS100
AS200
1
2
3
4
5
6
7
Notes: The LDP PHP behavior is not considered in data forwarding.

## Slide 16: Inter-AS VPN Option A Characteristics
Inter-AS VPN Option A is easy to configure and understand.
When there are a small number of VPNs on a network, inter-AS VPN Option A is applicable.
An ASBR views the peer ASBR as a CE and uses a VRF interface to connect to the peer ASBR. ASBRs in two ASs exchange VPNv4 routes.
At the data layer, VPN user data is exchanged between ASBRs in two ASs in the form of IP packets, that is, packets do not carry any label header.
The scalability of inter-AS VPN Option A is poor. ASBRs need to manage all VPN routes, and a VPN instance needs to be configured for each VPN. This results in numerous VPN-IPv4 routes on the ASBRs. In addition, because common IP forwarding is implemented between ASBRs, each inter-AS VPN requires a different interface, which can be a sub-interface, physical interface, or bundled logical interface. This poses high requirements for ASBRs. If a VPN spans multiple ASs, the intermediate ASs must support VPN services. This requires complex configurations and greatly affects the intermediate ASs. If only a few inter-AS VPN instances are used, inter-AS VPN Option A is recommended.

## Slide 17
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
  Fundamentals
  Basic Configurations
Fundamentals and Configurations of Inter-AS VPN Option B
Fundamentals and Configurations of Inter-AS VPN Option C

## Slide 18: Inter-AS VPN Option A Configuration Example (1)
CE1 and CE2 belong to the same VPN named vpna. CE1 and CE2 need to communicate with each other using Option A.
Device | Loopback0 | RD | RT
PE1 | 10.0.1.1/32 | 100:1 | 1:1
ASBR-PE1 | 10.0.3.3/32 | 100:3 | 1:1
ASBR-PE2 | 10.0.4.4/32 | 200:4 | 2:2
PE2 | 10.0.6.6/32 | 200:6 | 2:2
Data plan
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Configuration roadmap:
  Configure basic MPLS capabilities and MPLS LDP on the MPLS backbone network to establish LDP LSPs in each AS. (The configuration details are not provided here.)
  Establish an MP-IBGP peer relationship between the PE and ASBR-PE in each AS to exchange VPN routing information. (The configuration details are not provided here.)
  Configure a VPN instance on the PE connected to the CE in each AS and establish EBGP peer relationships between the PE and CE to exchange VPN routing information. (The configuration details are not provided here.)
  Create a VPN instance on each ASBR-PE, bind the instance to the interface connected to the other ASBR-PE (viewed as a CE), and establish an EBGP peer relationship between the ASBR-PEs to exchange VPN routing information.

## Slide 19: Inter-AS VPN Option A Configuration Example (2)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Take ASBR-PE1 as an example to create a VPN instance and bind it to the interface connected to ASBR-PE2.
[ASBR-PE1] ip vpn-instance vpna
[ASBR-PE1-vpn-instance-vpna] ipv4-family
[ASBR-PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:3
[ASBR-PE1-vpn-instance-vpna-af-ipv4] vpn-target 1:1 both
[ASBR-PE1-vpn-instance-vpna-af-ipv4] quit
[ASBR-PE1-vpn-instance-vpna] quit
[ASBR-PE1] interface gigabitethernet 2/0/0
[ASBR-PE1-GigabitEthernet2/0/0] ip binding vpn-instance vpna
[ASBR-PE1-GigabitEthernet2/0/0] ip address 10.0.34.3 24
[ASBR-PE1-GigabitEthernet2/0/0] quit
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.1.1 as-number 100
[ASBR-PE1-bgp] peer 10.0.1.1 connect-interface loopback 0
[ASBR-PE1-bgp] ipv4-family vpnv4
[ASBR-PE1-bgp-af-vpnv4] peer 10.0.1.1 enable
[ASBR-PE1-bgp-af-vpnv4] quit
[ASBR-PE1-bgp] quit
Take ASBR-PE1 as an example to establish an MP-IBGP peer relationship between ASBR-PE1 and PE1.
ASBR-PE1 establishes a VPNv4 peer relationship with PE1 to transmit VPNv4 routes.
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] ipv4-family vpn-instance vpna
[ASBR-PE1-bgp-vpna] peer 10.0.34.4 as-number 200
[ASBR-PE1-bgp-vpna] import-route direct
[ASBR-PE1-bgp-vpna] quit
[ASBR-PE1-bgp] quit
Take ASBR-PE1 as an example to establish an EBGP peer relationship between ASBR-PE1 and ASBR-PE2.
ASBR-PE1 views ASBR-PE2 as a CE and establishes an EBGP peer relationship with ASBR-PE2 in the VPN instance address family view to transmit IPv4 routes.

## Slide 20: Verifying the Configuration (1)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Check CE1's routing information on PE1.
<PE1>display bgp vpnv4 all routing-table
Total number of routes from all PE: 1
Route Distinguisher: 100:1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 192.168.1.0 10.0.11.1 0 0 65000i
VPN-Instance vpna, Router ID 10.0.12.1:
Total Number of Routes: 1
Network NextHop MED LocPrf PrefVal Path/Ogn
*> 192.168.1.0 10.0.11.1 0 0 65000i
Check CE1's routing information on ASBR-PE1.
<ASBR-PE1>display bgp vpnv4 all routing-table 192.168.1.0
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): 1026/NULL
From: 10.0.1.1 (10.0.1.1)
Route Duration: 00h05m07s
Relay IP Nexthop: 10.0.23.2
Relay token: 0x1
Original nexthop: 10.0.1.1
Ext-Community:RT <1 : 1>
AS-path 65000, origin igp, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 2
The next hop is PE1.
<ASBR-PE2>display bgp vpnv4 all routing-table 192.168.1.0
Total routes of Route Distinguisher(100:4): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): NULL/1027
From: 10.0.34.3 (10.0.3.3)
Route Duration: 00h13m13s
Direct Out-interface: GigabitEthernet0/0/1
Original nexthop: 10.0.34.3
Ext-Community:RT <2 : 2>
Check CE1's routing information on ASBR-PE2.
The next hop is ASBR-PE1.
The label of the received route is null, indicating that the route is an IPv4 route.
1
2
3
The next hop is CE1.

## Slide 21: Verifying the Configuration (2)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Check CE1's routing information on PE2.
<PE2>display bgp vpnv4 all routing-table 192.168.1.0
Total routes of Route Distinguisher(100:4): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): 1027/NULL
From: 10.0.4.4 (10.0.4.4)
Relay IP Nexthop: 10.0.56.5
Relay IP Out-Interface: GigabitEthernet0/0/1
Relay Tunnel Out-Interface: GigabitEthernet0/0/1
Relay token: 0x1
Original nexthop: 10.0.4.4
Qos information : 0x0
Ext-Community:RT <2 : 2>
ASBR-PE2 allocates label 1027 to the route.
Check CE1's routing information on CE2.
<CE2>display bgp routing-table 192.168.1.0
BGP local router ID : 10.0.26.2
Local AS number : 65001
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 192.168.1.0/24:
From: 10.0.26.6 (10.0.6.6)
Direct Out-interface: GigabitEthernet0/0/0
Original nexthop: 10.0.26.6
AS-path 200 100 65000, origin igp, pref-val 0, valid, external, best, select,
The next hop is PE2.
<CE2>ping -a 192.168.2.1 192.168.1.1
PING 192.168.1.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.1.1: bytes=56 Sequence=1 ttl=250 time=100 ms
Reply from 192.168.1.1: bytes=56 Sequence=2 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=3 ttl=250 time=50 ms
Reply from 192.168.1.1: bytes=56 Sequence=4 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=5 ttl=250 time=60 ms
Ping 192.168.1.1 from CE2.
1
2
3
4
5

## Slide 22
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
Fundamentals and Configurations of Inter-AS VPN Option B
  Fundamentals
  Basic Configurations
Fundamentals and Configurations of Inter-AS VPN Option C

## Slide 23: Inter-AS VPN Option B Overview
Compared with Option A, Option B does not require VPN instances to be created on ASBR-PEs and does not require interfaces to be bound.
In Option B, two ASBRs use MP-EBGP to exchange VPNv4 routes received from the PEs in their respective ASs.
By default, a PE stores only the VPN routes that match the VPN targets of its local VPN instances. Therefore, ASBRs can be configured not to filter routes based on RTs.
On a large-scale network, RRs can be deployed to transmit user-side VPN routes.
P1
ASBR-PE1
PE1
CE1
AS100
P2
PE2
ASBR-PE2
CE2
AS200
MP-EBGP
VPNv4 route transmission
If ASBRs are not directly connected to CEs, VPN instances do not need to be created.
To disable VPN target-based filtering for received VPN routes, run the undo policy vpn-target command.
Interfaces connecting two ASBRs must support MPLS forwarding.

## Slide 24: Inter-AS VPN Option B Topology
A PE uses MP-IBGP to advertise a VPNv4 route to the ASBR-PE or VPN RR (with the ASBR-PE as the client) in the same AS. The ASBR-PE uses MP-EBGP to advertise the VPNv4 route to the peer ASBR-PE in another AS, and then the peer ASBR-PE advertises the VPNv4 route to the PE in the same AS.
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
IP/MPLS
Site1
Site2
MP-IBGP
IP/MPLS
MP-IBGP
P1
P2
AS100
AS200
EBGP

## Slide 25: Inter-AS VPN Option B: Control Plane Without RRs
CE1 advertises an IPv4 route to PE1.
PE1 converts the IPv4 route into a VPNv4 route, sets the next hop of the route to PE1, allocates the VPN label V1 to the route, and advertises the route to ASBR-PE1.
ASBR-PE1 changes the next hop of the route to itself, allocates a new VPN label V2 to the route, and uses MP-EBGP to advertise the route for the prefix Net1 to ASBR-PE2.
ASBR-PE2 sets the next hop of the route to itself, allocates the VPN label V3 to the route, and uses MP-IBGP to advertise the route for the prefix Net1 to PE2.
PE1 and P1 allocate tunnel labels T1 and T2 respectively to the routes destined for PE1.
ASBR-PE2 and P2 allocate tunnel labels T3 and T4 respectively to the routes destined for ASBR-PE2.
PE2 converts the VPNv4 route into an IPv4 route, sets the next hop to PE2, and advertises the route to CE2.
IPv4 routing
Tunnel label
Tunnel label
VPNv4 routing
VPNv4 routing
IPv4 routing
Tunnel label
Tunnel label
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
Site1
Site2
FEC: PE1
Label: T1
FEC: PE1
Label: T2
VPNv4: RD1+Net1
NH: PE1
VPN label: V1
IPv4: Net1
NH: CE1
FEC: ASBR-PE2
Label: T3
FEC: ASBR-PE2
Label: T4
VPNv4 routing
VPNv4: RD1+Net1
NH: ASBR-PE2
VPN label: V3
IPv4: Net1
NH: PE2
Net1
MP-IBGP
MP-IBGP
EBGP
VPNv4: RD1+Net1
NH: ASBR-PE1
VPN label: V2
P1
P2
AS100
AS200
1
2
3
4
7
5
5
6
6

## Slide 26: Inter-AS VPN Option B: Control Plane with RRs
When there are a large number of VPN instances, RRs can be deployed. As shown in the figure, the PEs and ASBRs in ASs establish MP-BGP peer relationships only with RRs, and the RRs are responsible for reflecting routes. The PEs and ASBRs do not need to establish BGP peer relationships with each other.
The RRs are responsible only for transmitting VPNv4 routes on the control plane. During data forwarding, traffic does not pass through the RRs.
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
Site1
Site2
Net1
P1
P2
RR1
RR2
EBGP
MP-IBGP
Reflects routes without forwarding data.
Notes: In the inter-AS VPN scenario, it is recommended that independent RRs be deployed to transmit routes only without forwarding traffic.

## Slide 27: Inter-AS VPN Option B: Forwarding Plane
CE2 sends an IP packet destined for Net1 to PE2.
After PE2 receives the IP packet, it encapsulates the packet with a VPN label V3 and then an outer label T4 and forwards the packet to P2.
P2 swaps the outer label T4 with T3 and forwards the packet to ASBR-PE2.
ASBR-PE2 removes the outer label, swaps the VPN label V3 with V2, and forwards the packet to ASBR-PE1. In this case, the packet carries only one VPN label.
ASBR-PE1 swaps the VPN label V2 with V1, adds the outer label T2 to the packet, and forwards the packet to P1.
P1 swaps the outer label T2 with T1 and forwards the packet to PE1.
PE1 removes all labels from the packet and forwards the packet (a common IP packet) to CE1.
IP
MPLS
MPLS
MPLS
MPLS
PE1
PE2
ASBR-PE1
ASBR-PE2
CE1
CE2
Site1
Site2
Net1
Net1
IP/MPLS
MP-IBGP
IP/MPLS
MP-IBGP
Net1
V3
T4
Net1
V3
T3
MPLS
Net1
Net1
V1
T2
Net1
V1
T1
Net1
V2
EBGP
IP
P1
P2
AS100
AS200
1
2
3
4
5
6
7

## Slide 28: Inter-AS VPN Option B Characteristics
The advantage of Option B is that all traffic is forwarded by ASBRs. In this way, traffic is controllable, but the loads on the ASBRs are heavy because the ASBRs need to save a large number of VPNv4 routes. BGP routing policies, such as VPN target-based filtering policies, can be configured on ASBRs, so that ASBRs only save some of VPNv4 routes.
The disadvantage is that VPN routing information is stored on and forwarded by ASBRs. If a large number of VPN routes exist, the overloaded ASBRs tend to become faulty points. Therefore, in scenarios where MP-EBGP is used, ASBRs that maintain VPN routing information generally do not perform IP forwarding on the public network.
Option B is better than Option A when a large number of VRF instances need to communicate with each other.

## Slide 29
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
Fundamentals and Configurations of Inter-AS VPN Option B
  Fundamentals
  Basic Configurations
Fundamentals and Configurations of Inter-AS VPN Option C

## Slide 30: Inter-AS VPN Option B Configuration Example (1)
CE1 and CE2 belong to the same VPN named vpna. CE1 and CE2 need to communicate with each other using Option B.
Device | Loopback0 | RD | RT
PE1 | 10.0.1.1/32 | 100:1 | 1:1
ASBR-PE1 | 10.0.3.3/32 | / | /
ASBR-PE2 | 10.0.4.4/32 | / | /
PE2 | 10.0.6.6/32 | 200:6 | 1:1
Data plan
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Configuration roadmap
  Configure basic MPLS capabilities and MPLS LDP on the MPLS backbone network to establish LDP LSPs in each AS. (The configuration details are not provided here.)
  Establish an MP-IBGP peer relationship between the PE and ASBR-PE in each AS to exchange VPN routing information. (The configuration details are not provided here.)
  Configure a VPN instance on the PE connected to the CE in each AS and establish EBGP peer relationships between the PE and CE to exchange VPN routing information. (The configuration details are not provided here.)
  Enable MPLS on the interfaces connecting the ASBRs, establish an MP-EBGP peer relationship between the ASBRs, and configure the ASBRs not to filter received VPNv4 routes based on RTs.
RT values of PE1 and PE2 must match.

## Slide 31: Inter-AS VPN Option B Configuration Example (2)
PE1
CE1
PE2
CE1
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Take ASBR-PE1 as an example to establish an MP-EBGP peer relationship between ASBR-PE1 and ASBR-PE2, configure ASBR-PE1 not to filter received VPNv4 routes based on the VPN target, and enable ASBR-PE1 to allocate labels based on the next hop.
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.34.4 as-number 200
[ASBR-PE1-bgp] ipv4-family vpnv4
[ASBR-PE1-bgp-af-vpnv4] peer 10.0.34.4 enable
[ASBR-PE1-bgp-af-vpnv4] undo policy vpn-target
[ASBR-PE1-bgp-af-vpnv4] apply-label per-nexthop
[ASBR-PE1-bgp-af-vpnv4] quit
[ASBR-PE1-bgp] quit
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.1.1 as-number 100
[ASBR-PE1-bgp] peer 10.0.1.1 connect-interface loopback 0
[ASBR-PE1-bgp] ipv4-family vpnv4
[ASBR-PE1-bgp-af-vpnv4] peer 10.0.1.1 enable
[ASBR-PE1-bgp-af-vpnv4] quit
[ASBR-PE1-bgp] quit
Take ASBR-PE1 as an example to establish an MP-IBGP peer relationship between ASBR-PE1 and PE1.
[ASBR-PE1] interface gigabitethernet 2/0/0
[ASBR-PE1-GigabitEthernet2/0/0] mpls
[ASBR-PE1-GigabitEthernet2/0/0] quit
Take ASBR-PE1 as an example to enable MPLS on the interfaces connecting ASs.
By default, an ASBR allocates a label to each VPNv4 route to be advertised to its MP-BGP peers. After this command is run, ASBR-PE1 allocates a label to the routes with the same next hop and outgoing label.
To differentiate between VPN instances, ASBRs advertise VPNv4 routes to each other. Because the VPNv4 routes carry label information, the interfaces connecting ASBRs must support label forwarding.

## Slide 32: Verifying the Configuration (1)
The process of transmitting intra-area routing information is not described here. This example describes only the key procedure of transmitting routing information.
Check CE1's routing information on ASBR-PE1.
<ASBR-PE1>display bgp vpnv4 all routing-table 192.168.1.0
BGP local router ID : 10.0.3.3
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): 1026/1026
From: 10.0.1.1 (10.0.1.1)
Route Duration: 00h07m32s
Relay IP Nexthop: 10.0.23.2
Relay IP Out-Interface: GigabitEthernet0/0/0
Relay Tunnel Out-Interface: GigabitEthernet0/0/0
Relay token: 0x2
Original nexthop: 10.0.1.1
Qos information : 0x0
Ext-Community:RT <1 : 1> # The export RT value must match the import RT value of PE2.
AS-path 65000, origin igp, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 2
Advertised to such 1 peers:
10.0.34.4
PE1 allocates the label 1026 to the route. When routes are transmitted between ASs, ASBR-PE1 changes the next hop to itself. Therefore, ASBR-PE1 re-allocates the label 1026 when advertising routes to ASBR-PE2. MPLS labels are local to a device, so different devices can allocate the same label.
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24

## Slide 33: Verifying the Configuration (2)
Check CE1's routing information on ASBR-PE2.
<ASBR-PE2>display bgp vpnv4 all routing-table 192.168.1.0
BGP local router ID : 10.0.4.4
Local AS number : 200
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): 1026/1032
From: 10.0.34.3 (10.0.3.3)
Route Duration: 00h02m18s
Relay Tunnel Out-Interface: GigabitEthernet0/0/1
Relay token: 0x1
Original nexthop: 10.0.34.3
Qos information : 0x0
Ext-Community:RT <1 : 1>
AS-path 100 65000, origin igp, pref-val 0, valid, external, best, select, pre 2
55
Advertised to such 1 peers:
10.0.6.6
ASBR-PE1 allocates the label 1026 to the route. When advertising the route to PE2, ASBR-PE2 changes the next hop of the route to itself and re-allocates the label 1032 to the route.
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24

## Slide 34: Verifying the Configuration (3)
Ping 192.168.1.1 from CE2.
<CE2>ping -a 192.168.2.1 192.168.1.1
PING 192.168.1.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.1.1: bytes=56 Sequence=1 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=2 ttl=250 time=50 ms
Reply from 192.168.1.1: bytes=56 Sequence=3 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=4 ttl=250 time=60 ms
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24

## Slide 35
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
Fundamentals and Configurations of Inter-AS VPN Option B
Fundamentals and Configurations of Inter-AS VPN Option C
  Fundamentals
  Basic Configurations

## Slide 36: Inter-AS VPN Option C Overview
In Option C, ASBRs do not store VPNv4 routes or advertise VPNv4 routes to each other. This is different from the implementation in Option A and Option B.
In Option C, PEs in different ASs establish a multi-hop EBGP connection with each other to exchange VPNv4 routes. Two solutions are available to enable PEs to communicate with each other:
  Solution 1: An ASBR uses BGP to send the routes destined for a PE in another AS to the local PE.
  Solution 2: An ASBR imports the routes destined for a PE in another AS to an IGP.
ASBRs do not have VPNv4 routes. To prevent routing blackholes during packet forwarding, PEs need to transmit packets over tunnels so that non-PE devices are unaware of VPN encapsulation information. Therefore, both the solutions require ASBRs to advertise labeled routes to set up outer forwarding tunnels between ASs.
P1
ASBR1
PE1
CE1
P2
PE2
ASBR2
CE2
AS200
EBGP
AS100
MP-EBGP
Advertise labeled routes
Solution 1
An ASBR uses BGP to advertise the routes destined for the peer PE.
Solution 2
An ASBR imports the routes destined for the peer PE to an IGP.

## Slide 37: Inter-AS VPN Option C Topology (Solution 1)
ASBRs do not maintain or advertise VPNv4 routes. ASBRs only need to maintain labeled routes destined for PEs and use EBGP to advertise these labeled routes to the peer ASBRs in other ASs. ASBRs in the transit AS also need to use EBGP to advertise labeled IPv4 routes. In this way, a VPN LSP needs to be established between the ingress and egress PEs so that a multi-hop MP-EBGP connection can be established between the PEs to advertise VPNv4 routes.
To further improve performance, a multi-hop MP-EBGP session can be established between VPN RRs in different ASs. When these VPN RRs advertise VPNv4 routes, the next-hop information of these routes remains unchanged. PEs establish MP-IBGP sessions only with VPN RRs.
PE1
PE2
ASBR1
ASBR2
CE1
CE2
Site1
Site2
EBGP
P1
P2
AS100
AS200
Solution 2
Solution 1
IPv4
VPN
LDP LSP
BGP LSP
Notes: If the P device of each AS knows the routes to the PEs of other ASs, the data forwarding process will be relatively simple. But if the P device does not know these routes, then when a PE receives VPN data from a CE, the PE will add three labels. The bottom label is the VPN label that is allocated by the peer PE and associated with VPN routes, the middle label is the label allocated by an ASBR and associated with the route to the peer PE, and the outer label is the label associated with the route to the next-hop ASBR.
Note: For convenience, as shown in the figure above, a symmetric LSP is used for illustration, but in fact, in the working process of the control plane and the data plane, the LSP of the ASs at both ends is asymmetric.

## Slide 38: Inter-AS VPN Option C (Solution 1): Without RRs
CE1 advertises an IPv4 route to PE1.
PE1 converts the IPv4 route into a VPNv4 route, sets the next hop of the route to PE1, allocates the VPN label V1 to the route, and advertises the route to PE2.
ASBR1 advertises a labeled IPv4 route destined for PE1 to ASBR2 through an EBGP session. The next hop of the route is ASBR1, and the label is the BGP label B1.
ASBR2 advertises a labeled IPv4 route destined for PE1 to PE2 through a BGP session. The next hop of the route is ASBR2, and the label is the BGP label B2.
PE1 and P1 allocate tunnel labels T1 and T2 respectively to the routes destined for PE1.
ASBR2 and P2 allocate tunnel labels T3 and T4 respectively to the routes destined for ASBR2.
PE2 converts the VPNv4 route into an IPv4 route, sets the next hop to PE2, and advertises the route to CE2.
IPv4 routing
Tunnel label
Tunnel label
BGP labeled IPv4
IPv4 routing
Tunnel label
Tunnel label
CE1
CE2
Site1
Site2
FEC: PE1
Label: T1
VPNv4: RD1+Net1
NH: PE1
VPN label: V1
IPv4: Net1
NH: CE1
BGP labeled IPv4
IPv4: Net1
NH: PE2
Net1
PE1
PE2
ASBR1
ASBR2
IP/MPLS
EBGP
IP/MPLS
FEC: PE1
Label: T2
FEC: ASBR2
Label: T3
FEC: ASBR2
Label: T4
NLRI: PE1
Label: B2
NH: ASBR2
NLRI: PE1
Label: B1
NH: ASBR1
VPNv4 routing
P1
P2
AS100
AS200
1
2
3
4
5
5
6
6
7
Solution 2
Solution 1

## Slide 39: Inter-AS VPN Option C (Solution 1): With RRs
The local PE establishes a VPNv4 peer relationship only with the local RR, and the local RR establishes a VPNv4 peer relationship with the peer RR to transmit inter-AS VPN routes.
ASBRs and PEs establish BGP unicast IPv4 peer relationships with RRs.
  An ASBR learns the route destined for the peer RR's loopback interface from the peer ASBR and transmits the route to the local RR so that the local RR can establish a VPNv4 peer relationship with the peer RR.
  An ASBR learns the routes destined for the peer RR and PE's loopback interfaces from the peer ASBR and transmits the routes to the local RR, which then transmits the routes to the local PE. In this way, the local PE can establish a BGP LSP with the peer PE in another AS.
PE1
PE2
ASBR1
ASBR2
CE1
CE2
Site1
Site2
Net1
P1
P2
RR1
RR2
Unicast BGP peer relationship
MP-BGP
Reflects routes without forwarding data.
Solution 2
Solution 1

## Slide 40: Inter-AS VPN Option C (Solution 1): Forwarding Plane
CE2 sends an IP packet destined for Net1 to PE2.
After receiving the IP packet, PE2 encapsulates the packet with the following three labels in sequence: the VPN label V1, the BGP label B2 allocated by ASBR2, and the outer label T4.
P2 swaps the outer label T4 with T3 and forwards the packet to ASBR2.
ASBR2 removes the outer label, swaps the BGP label B2 with B1, and forwards the packet to ASBR1.
After receiving the packet, ASBR1 removes the BGP label B1 and checks its forwarding table. It finds the label T2 associated with the route destined for PE1, adds T2 to the top of the label stack, and forwards the packet to P1.
P1 swaps the outer label T2 with T1 and forwards the packet to PE1.
PE1 removes all labels from the packet and forwards the packet to CE1.
IP
MPLS
MPLS
MPLS
MPLS
IP
Net1
Net1
V1
B2
Net1
V1
B2
MPLS
Net1
Net1
V1
T2
Net1
V1
T1
Net1
V1
PE1
PE2
ASBR1
ASBR2
IP/MPLS
MP-EBGP
IP/MPLS
T4
T3
B1
P1
P2
AS100
AS200
CE1
Site1
Net1
CE2
Site2
2
1
3
4
5
6
7
Solution 2
Solution 1

## Slide 41: Inter-AS VPN Option C (Solution 1) FAQ (1)
Why does ASBR2 allocate labels to the routes destined for PE1? (P2 is not considered at present.)
  ASBR2 is unaware of VPN routes. Therefore, when a packet carrying only the VPN label (allocated by PE1) arrives at ASBR2, ASBR2 cannot identify the packet and discards it.
ASBR2
P2
PE2
CE2
IP
Net1
MPLS
Net1
V1
ASBR1
ASBR2
P2
PE2
CE2
IP
Net1
MPLS
ASBR1
IP
Why does ASBR1 allocate labels to the routes destined for PE1?
  ASBR1 is unaware of VPN routes. Therefore, when a packet carrying only the VPN label (allocated by PE1) arrives at ASBR1, ASBR1 cannot identify the packet and discards it.
Net1
V1
Net1
V1
B2
Solution 2
Solution 1

## Slide 42: Inter-AS VPN Option C (Solution 1) FAQ (2)
Why does P2 allocate labels to ASBR2?
  P2 does not identify the routing information of PE1. Therefore, when a VPN packet carrying the outer BGP label (allocated by ASBR2) arrives at P2, P2 cannot identify the outer label B2 and discards the packet.
ASBR2
P2
PE2
CE2
IP
Net1
ASBR1
Net1
V1
B2
MPLS
Let's review the basic characteristics of VPN.
  Private: It provides the same private network as a traditional private network. Resources between the VPN and the underlying bearer network are independent, that is, resources in a VPN are not used by users who do not belong to the VPN or non-VPN users. In addition, VPN security can be fully guaranteed to protect internal information of the VPN against external interference.
  Virtual: VPN users communicate over a public network, which is also used by other non-VPN users. That is, a VPN user obtains a logical private network. A public network that carries a VPN is called a VPN backbone network.
To achieve the two characteristics, only PEs are aware of VPN routing information. To prevent packet loss caused by routing blackholes during data forwarding, VPN data needs to be carried over various types of tunnels.
Common tunneling technologies include MPLS, GRE, and Segment Routing over IPv6 (SRv6).
Solution 2
Solution 1

## Slide 43: Inter-AS VPN Option C (Solution 2)
Solution 2 is similar to solution 1.
Three labels (VPN label, BGP LSP label, and tunnel LSP label) are used in solution 1, whereas only two labels (VPN label and tunnel label) are used in solution 2.
In solution 1, a policy needs to be configured on the local ASBR to generate a new label. After the local ASBR receives a labeled BGP route from the peer ASBR, the local ASBR allocates a new label to the BGP route and advertises the route to the PE or RR in the same AS so that a complete BGP LSP can be established. In solution 2, MPLS needs to be configured on an ASBR to allocate labels to labeled BGP routes. On the PE in the same AS as the ASBR, you can view the LDP LSP to the peer PE instead of a BGP LSP.
RRs can be deployed in both solution 1 and solution 2.
Solution 2
Solution 1

## Slide 44: Inter-AS VPN Option C (Solution 2) Topology
Solution 2: ASBRs do not maintain or advertise VPNv4 routes. ASBRs only need to maintain labeled routes destined for PEs and use EBGP to advertise these labeled routes to the peer ASBRs. After the peer ASBR receives a labeled BGP route, LDP triggers the generation of a label for the route and transmits the label between LDP peers in the same AS. Therefore, on a PE, you can view the LDP LSP to the peer PE.
To further improve performance, a multi-hop MP-EBGP session can be established between VPN RRs in different ASs. A PE in an AS only needs to establish an MP-IBGP peer relationship with an RR in the AS. When advertising VPNv4 routes, the VPN RRs do not change the next-hop information. In this manner, when the peer PE forwards traffic, the traffic can be recursed to the correct tunnel.
PE1
PE2
ASBR1
ASBR2
CE1
CE2
Site1
Site2
EBGP
P1
P2
AS100
AS200
IPv4
VPN
LDP LSP
BGP LSP
Solution 2
Solution 1

## Slide 45: Inter-AS VPN Option C (Solution 2): Without RRs
CE1 advertises an IPv4 route to PE1.
PE1 converts the IPv4 route into a VPNv4 route, sets the next hop of the route to PE1, allocates the VPN label V1 to the route, and advertises the route to PE2.
PE1 and P1 allocate tunnel labels T1 and T2 respectively to the routes destined for PE1.
ASBR1 advertises the labeled IPv4 route destined for PE1 to ASBR2 through an EBGP session. The next hop of the route is ASBR1, and the label is the BGP label B1.
ASBR2 and P2 allocate tunnel labels T3 and T4 respectively to the routes destined for PE1.
PE2 converts the VPNv4 route into an IPv4 route, sets the next hop to PE2, and advertises the route to CE2.
IPv4 routing
BGP labeled IPv4
IPv4 routing
Tunnel label
Tunnel label
CE1
CE2
Site1
Site2
FEC: PE1
Label: T1
VPNv4: RD1+Net1
NH: PE1
VPN label: V1
IPv4: Net1
NH: CE1
IPv4: Net1
NH: PE2
Net1
PE1
PE2
ASBR1
ASBR2
IP/MPLS
IP/MPLS
FEC: PE1
Label: T2
NLRI: PE1
Label: B1
NH: ASBR1
VPNv4 routing
P1
P2
AS100
AS200
1
2
4
5
3
3
6
Tunnel label
Tunnel label
FEC: PE1
Label: T3
FEC: PE1
Label: T4
5
Solution 2
Solution 1

## Slide 46: Inter-AS VPN Option C (Solution 2): Control Plane with RRs
The local PE establishes a VPNv4 peer relationship only with the local RR, and the local RR establishes a VPNv4 peer relationship with the peer RR to transmit inter-AS VPN routes.
The RRs are responsible only for transmitting VPNv4 routes on the control plane. Traffic on the forwarding plane does not pass through the RRs.
PE1
PE2
ASBR1
ASBR2
CE1
CE2
Site1
Site2
Net1
P1
P2
RR1
RR2
Unicast BGP peer relationship
MP-BGP peer relationship
Reflects routes without forwarding data.
Solution 2
Solution 1

## Slide 47: Inter-AS VPN Option C (Solution 2) Forwarding Plane
CE2 sends an IP packet destined for Net1 to PE2.
After receiving the IP packet, PE2 encapsulates the packet with the VPN label V1. Because the next hop (PE1) of the packet destined for Net1 is not a directly connected neighbor, PE2 finds that the label of the packet destined for PE1 is T4 and encapsulates the packet with the label T4.
P2 swaps the outer label T4 with T3 and forwards the packet to ASBR2.
ASBR2 removes the outer label, swaps the label T3 with B1, and forwards the packet to ASBR1.
After receiving the packet, ASBR1 removes the label B1 and checks its forwarding table. It finds the label T2 associated with the route destined for PE1, adds T2 to the top of the label stack, and forwards the packet to P1.
P1 swaps the outer label T2 with T1 and forwards the packet to PE1.
PE1 removes all labels from the packet and forwards the packet to CE1.
IP
MPLS
MPLS
MPLS
MPLS
IP
Net1
Net1
V1
Net1
V1
MPLS
Net1
Net1
V1
T2
Net1
V1
T1
Net1
V1
PE1
PE2
ASBR1
ASBR2
IP/MPLS
IP/MPLS
T4
T3
B1
P1
P2
AS100
AS200
CE1
Site1
Net1
CE2
Site2
2
1
3
4
5
6
7
Solution 2
Solution 1

## Slide 48: Inter-AS VPN Option C Characteristics
VPN routes are directly exchanged between the ingress and egress PEs. The routes do not need to be stored or forwarded by intermediate devices.
Only PEs maintain VPN routing information, and Ps and ASBRs are only responsible for packet forwarding. This means that the intermediate devices only need to support MPLS forwarding instead of MPLS VPN services. ASBRs are no longer bottlenecks. Option C, therefore, is suitable for VPNs spanning multiple ASs.
MPLS VPN load balancing is easy to implement using Option C.
The disadvantage of Option C is that it costs too much to manage an end-to-end connection between PEs.

## Slide 49: Comparison of Three Inter-AS VPN Solutions
Inter-AS VPN Solution | Description
Option A | Easy configuration: MPLS is not required between ASBRs, and no special configuration is required for inter-AS connections. Poor scalability: ASBRs need to manage all VPN routes, and a VPN instance needs to be configured for each VPN. This results in numerous VPNv4 routes on the ASBRs. In addition, because common IP forwarding is implemented between ASBRs, each inter-AS VPN requires a different interface, which can be a sub-interface, physical interface, or bundled logical interface. This poses high requirements for ASBRs. If a VPN spans multiple ASs, the intermediate ASs must support VPN services. This requires complex configurations and greatly affects the intermediate ASs. If only a few inter-AS VPN instances are used, Option A is recommended.
Option B | Unlike Option A, Option B is not restricted by the number of links between ASBRs. If a large number of VPN routes exist, the overloaded ASBRs tend to become faulty points. Therefore, in scenarios where MP-EBGP is used, ASBRs that maintain VPN routing information generally do not perform IP forwarding on the public network.
Option C | VPN routes are directly exchanged between the ingress and egress PEs. The routes do not need to be stored or forwarded by intermediate devices. Only PEs maintain VPN routing information, and Ps and ASBRs are only responsible for packet forwarding. This means that the intermediate devices only need to support MPLS forwarding instead of MPLS VPN services. ASBRs are no longer bottlenecks. Option C, therefore, is suitable for VPNs spanning multiple ASs. MPLS VPN load balancing is easy to implement using Option C. The disadvantage of Option C is that it costs too much to manage an end-to-end BGP LSP between PEs.

## Slide 50
Background of Inter-AS VPN Solutions
Fundamentals and Configurations of Inter-AS VPN Option A
Fundamentals and Configurations of Inter-AS VPN Option B
Fundamentals and Configurations of Inter-AS VPN Option C
  Fundamentals
  Basic Configurations

## Slide 51: Option C (Solution 1) Configuration Example (1)
CE1 and CE2 belong to the same VPN named vpna. CE1 and CE2 need to communicate with each other using Option C (solution 1).
Device | Loopback0 | RD | RT
PE1 | 10.0.1.1/32 | 100:1 | 1:1
ASBR-PE1 | 10.0.3.3/32 | / | /
ASBR-PE2 | 10.0.4.4/32 | / | /
PE2 | 10.0.6.6/32 | 200:6 | 1:1
Data plan
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Configuration roadmap
  Configure basic MPLS capabilities and MPLS LDP on the MPLS backbone network to establish LDP LSPs in each AS. (The configuration details are not provided here.)
  Configure a VPN instance on the PE connected to the CE in each AS and establish EBGP peer relationships between the PE and CE to exchange VPN routing information. (The configuration details are not provided here.)
  Establish an MP-IBGP peer relationship between the PE and ASBR-PE in each AS to exchange labeled IPv4 routes.
  Enable each ASBR-PE to exchange labeled IPv4 routes with the peer ASBR PE.
  Configure route-policies on each ASBR-PE, so that it can allocate MPLS labels to the routes to be advertised to the peer ASBR and allocate new MPLS labels to the labeled IPv4 routes to be advertised to the PE in the same AS.
  Establish an MP-EBGP peer relationship between PEs in different ASs and set the maximum number of hops between the PEs.
RT values of PE1 and PE2 must match.
Solution 2
Solution 1

## Slide 52: Option C (Solution 1) Configuration Example (2)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.1.1 route-policy policy2 export
[ASBR-PE1-bgp] peer 10.0.1.1 label-route-capability
[ASBR-PE1-bgp] quit
On ASBR-PE1, apply the route-policy policy2 to the routes advertised to PE1 and enable the capability to exchange labeled IPv4 routes with PE1.
[ASBR-PE1] interface gigabitethernet 2/0/0
[ASBR-PE1-GigabitEthernet2/0/0] mpls # Interfaces between ASBRs support MPLS.
[ASBR-PE1-GigabitEthernet2/0/0] quit
On ASBR-PE1, enable MPLS on the interface connected to ASBR-PE2.
On ASBR-PE1, create route-policies.
[ASBR-PE1] route-policy policy1 permit node 1
[ASBR-PE1-route-policy] apply mpls-label
[ASBR-PE1-route-policy] quit
[ASBR-PE1] route-policy policy2 permit node 1
[ASBR-PE1-route-policy] if-match mpls-label
[ASBR-PE1-route-policy] apply mpls-label
[ASBR-PE1-route-policy] quit
The route-policy policy1 is used to advertise labeled routes to ASBR-PE2.
The route-policy policy2 is used to allocate BGP labels to the labeled routes received from ASBR-PE2.
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.34.4 route-policy policy1 export
[ASBR-PE1-bgp] peer 10.0.34.4 label-route-capability
[ASBR-PE1-bgp] quit
On ASBR-PE1, apply the route-policy policy1 to the routes advertised to ASBR-PE2 and enable the capability to exchange labeled IPv4 routes with ASBR-PE2.
In this example, the configuration of ASBR-PE1 is provided for your reference.
Solution 2
Solution 1

## Slide 53: Option C (Solution 1) Configuration Example (3)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
[PE1] bgp 100
[PE1-bgp] peer 10.0.6.6 as-number 200
[PE1-bgp] peer 10.0.6.6 connect-interface LoopBack 1
[PE1-bgp] peer 10.0.6.6 ebgp-max-hop 10
[PE1-bgp] ipv4-family vpnv4
[PE1-bgp-af-vpnv4] peer 10.0.6.6 enable
[PE1-bgp-af-vpnv4] quit
[PE1-bgp] quit
On PE1, enable it to establish an MP-EBGP peer relationship with PE2.
Configure ASBR-PE1 to advertise the route destined for PE1's loopback interface to ASBR-PE2, which then advertises the route to PE2.
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] network 10.0.1.1 32
[ASBR-PE1-bgp] quit
If there is no directly connected physical link between EBGP peers, the peer ebgp-max-hop command must be run to configure EBGP peers to establish TCP connections across multiple hops.
Solution 2
Solution 1

## Slide 54: Verifying the Configuration (1)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2./24
AS100
AS200
GE2/0/0
10.0.34.0/24
Check CE1's routing information on PE2.
<PE2>display bgp vpnv4 all routing-table 192.168.1.0
BGP local router ID : 10.0.6.6
Local AS number : 200
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 192.168.1.0/24:
Label information (Received/Applied): 1029/NULL
From: 10.0.1.1 (10.0.1.1)
Route Duration: 00h00m14s
Relay IP Nexthop: 10.0.56.5
Relay IP Out-Interface: GigabitEthernet0/0/1
Relay Tunnel Out-Interface: GigabitEthernet0/0/1
Relay token: 0x9
Original nexthop: 10.0.1.1
Qos information : 0x0
Ext-Community:RT <1 : 1>
AS-path 100 65000, origin igp, pref-val 0, valid, external, best, select, pre 255, IGP cost 2
PE1 allocates the label 1029 to the route.
PE1 directly sends the VPNv4 route to PE2.
1
Solution 2
Solution 1

## Slide 55: Verifying the Configuration (2)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Check information about routes destined for 10.0.1.1 on PE2.
<PE2>display bgp routing-table 10.0.1.1
BGP local router ID : 10.0.6.6
Local AS number : 200
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.0.1.1/32:
Label information (Received/Applied): 1032/NULL
From: 10.0.4.4 (10.0.4.4)
Route Duration: 00h07m52s
Relay IP Nexthop: 10.0.56.5
Relay IP Out-Interface: GigabitEthernet0/0/1
Relay Tunnel Out-Interface: GigabitEthernet0/0/1
Relay token: 0x1
Original nexthop: 10.0.4.4
Qos information : 0x0
AS-path 100, origin igp, MED 2, localpref 100, pref-val 0, valid, internal, bes
t, select, active, pre 255, IGP cost 2
Not advertised to any peer yet
ASBR-PE2 allocates the BGP label 1032 to the route destined for 10.0.1.1.
The next hop of the route to 10.0.1.1 is 10.0.4.4. Therefore, PE2 performs recursive query again.
2
1
Solution 2
Solution 1

## Slide 56: Verifying the Configuration (3)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Check information about routes destined for 10.0.4.4 on PE2.
<PE2>display fib 10.0.4.4
Route Entry Count: 1
Destination/Mask Nexthop Interface TunnelID
10.0.4.4/32 10.0.56.5 GE0/0/1 0x1
<PE2>display tunnel-info tunnel-id 1
Tunnel ID: 0x1
Tunnel Token: 1
Type: lsp
Destination: 10.0.4.4
Out Interface: GigabitEthernet0/0/1
Out Label: 1024
Next Hop: 10.0.56.5
Lsp Index: 6144
<PE2>display mpls lsp out-label 1024 verbose
No : 1
Fec : 10.0.4.4/32
Nexthop : 10.0.56.5
In-Label : NULL
Out-Label : 1024
In-Interface : ----------
Out-Interface : GigabitEthernet0/0/1
LspIndex : 6144
Token : 0x1
LsrType : Ingress
Label Operation : PUSH
Packets are transmitted to 10.0.4.4 over tunnel 1.
2
3
The label 1024 needs to be added to the packets reaching 10.0.4.4.
Based on steps 1, 2, and 3, the packets sent by PE2 should carry the following labels:
Label Value | Type | FEC | Label Allocation Device
1029 | VPN label | 192.168.1.0/24 | PE1
1032 | BGP label | 10.0.1.1/32 | ASBR-PE2
1024 | LDP label | 10.0.4.4/32 | P2
Note: Other devices are not described here.
1
Solution 2
Solution 1

## Slide 57: Verifying the Configuration (4)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Ping 192.168.1.1 from CE2.
<CE2>ping -a 192.168.2.1 192.168.1.1
PING 192.168.1.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.1.1: bytes=56 Sequence=1 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=2 ttl=250 time=50 ms
Reply from 192.168.1.1: bytes=56 Sequence=3 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=4 ttl=250 time=60 ms
Solution 2
Solution 1

## Slide 58: Summary of Key Configurations for Inter-AS VPN Option C (Solution 1)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
Device | Key Points
PE1 PE2 | Enable PEs to exchange labeled IPv4 routes with the ASBR-PEs in the same AS. Enable PEs to establish multi-hop MP-EBGP peer relationships with the PEs in other ASs.
ASBR-PE1 ASBR-PE2 | Enable ASBR-PEs to exchange labeled IPv4 routes with ASBR-PEs in other ASs. Enable ASBR-PEs to exchange labeled IPv4 routes with the PEs in the same AS. Enable MPLS on the interfaces connecting ASBRs.
Solution 2
Solution 1

## Slide 59: Option C (Solution 2) Configuration Example (1)
CE1 and CE2 belong to the same VPN named vpna. CE1 and CE2 need to communicate with each other using Option C (solution 1). RR1 and RR2 reflect routes but do not forward traffic.
Device | Loopback0 | RD | RT
PE1 | 10.0.1.1/32 | 100:1 | 1:1
ASBR-PE1 | 10.0.3.3/32 | / | /
ASBR-PE2 | 10.0.4.4/32 | / | /
PE2 | 10.0.6.6/32 | 200:6 | 1:1
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
MP-EBGP
Configuration roadmap
  Configure basic MPLS capabilities and MPLS LDP on the MPLS backbone network to establish LDP LSPs in each AS. (The configuration details are not provided here.)
  Configure a VPN instance on the PE connected to the CE in each AS and establish EBGP peer relationships between the PE and CE to exchange VPN routing information.
  Advertise the routes of a PE in an AS to the peer PE: Configure the local ASBR-PE to advertise the routes of a PE in the local AS to the peer ASBR-PE using BGP, import BGP routes into an IGP on the peer ASBR-PE so that the peer PE can use an IGP to learn the routes of the PE in the same AS.
  Enable ASBR-PE1 and ASBR-PE2 to exchange labeled IPv4 routes.
  Configure ASBR-PEs to establish LDP LSPs for labeled BGP routes of the public network.
  Establish an MP-EBGP peer relationship between RRs in different ASs and set the maximum number of hops between the RRs.
Device | Loopback0
RR1 | 10.0.7.7/32
RR2 | 10.0.8.8/32
Solution 2
Solution 1

## Slide 60: Option C (Solution 2) Configuration Example (2)
On RR1, configure RR1 to establish VPNv4 peer relationships with RR2 and PE1, and configure RR1 not to change the next hops of routes.
[RR1] bgp 100
[RR1-bgp] peer 10.0.8.8 as-number 200
[RR1-bgp] peer 10.0.8.8 connect-interface LoopBack 1
[RR1-bgp] peer 10.0.8.8 EBGP-max-hop 100
[RR1-bgp] peer 10.0.1.1 as-number 100
[RR1-bgp] peer 10.0.1.1 connect-interface LoopBack 1
[RR1-bgp] ipv4-family vpnv4
[RR1-bgp-af-vpnv4] undo policy vpn-target
[RR1-bgp-af-vpnv4] peer 10.0.8.8 enable
[RR1-bgp-af-vpnv4] peer 10.0.8.8 next-hop-invariable
[RR1-bgp-af-vpnv4] peer 10.0.1.1 enable
[RR1-bgp-af-vpnv4] peer 10.0.1.1 next-hop-invariable
[RR1-bgp-af-vpnv4] quit
[RR1-bgp] quit
Configure RR1 not to change the next hops of routes so that traffic does not pass through RR1. That is, RR1 only reflects routes without forwarding traffic.
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
MP-EBGP
On ASBR-PE1, create a route-policy.
[ASBR-PE1] route-policy policy1 permit node 1
[ASBR-PE1-route-policy] apply mpls-label
[ASBR-PE1-route-policy] quit
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] peer 10.0.34.4 route-policy policy1 export
[ASBR-PE1-bgp] peer 10.0.34.4 label-route-capability
[ASBR-PE1-bgp] quit
On ASBR-PE1, apply the route-policy to the routes advertised to ASBR-PE2 and enable the capability to exchange labeled IPv4 routes with ASBR-PE2.
On ASBR-PE1, advertise the routes destined for the loopback interfaces of PE1 and RR1 to ASBR-PE2.
[ASBR-PE1] bgp 100
[ASBR-PE1-bgp] network 10.0.1.1 32 # Required for data forwarding
[ASBR-PE1-bgp] network 10.0.7.7 32
[ASBR-PE1-bgp] quit
Enable RR2 to learn the route to RR1 and establish a VPNv4 neighbor relationship.
Solution 2
Solution 1

## Slide 61: Option C (Solution 2) Configuration Example (3)
On ASBR-PE1, import BGP routes into an IGP.
[ASBR-PE1] ospf 1
[ASBR-PE1-ospf-1] import-route bgp
[ASBR-PE1-ospf-1] quit
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
On ASBR-PE1, establish LDP LSPs for labeled BGP routes of the public network.
[ASBR-PE1] mpls
[ASBR-PE1-mpls] lsp-trigger bgp-label-route
[ASBR-PE1-mpls] quit
Solution 2
Solution 1

## Slide 62: Verifying the Configuration (1)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
Check CE1's routing information on PE2.
<PE2>display ip routing-table vpn-instance vpna 192.168.1.0 verbose
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 192.168.1.0/24
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 10.0.1.1 Neighbour: 10.0.8.8
State: Active Adv Relied Age: 00h00m05s
Tag: 0 Priority: low
Label: 1028 QoSInfo: 0x0
IndirectID: 0x12
RelayNextHop: 10.0.56.5 Interface: GigabitEthernet0/0/1
TunnelID: 0xe Flags: RD
The route is learned from RR2 and its next hop is 10.0.1.1.
Solution 2
Solution 1

## Slide 63: Verifying the Configuration (2)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
Check information about routes destined for 10.0.1.1 (PE1) on PE2.
<PE2>display fib 10.0.1.1
Route Entry Count: 1
Destination/Mask Nexthop Interface TunnelID
10.0.1.1/32 10.0.56.5 GE0/0/1 0xe
<PE2>display tunnel-info tunnel-id e
Tunnel ID: 0xe
Tunnel Token: 14
Type: lsp
Destination: 10.0.1.1
Out Interface: GigabitEthernet0/0/1
Out Label: 1028
Next Hop: 10.0.56.5
Lsp Index: 6151
<PE2>display mpls lsp out-label 1028 verbose
No : 1
Fec : 10.0.1.1/32
Nexthop : 10.0.56.5
In-Label : NULL
Out-Label : 1028
LspIndex : 6151
Token : 0xe
LsrType : Ingress
Label Operation : PUSH
Based on steps 1 and 2, the packets sent by PE2 should carry the following labels:
Label Value | Type | FEC | Label Allocation Device
1028 | VPN label | 192.168.1.0/24 | PE1
1028 | LDP label | 10.0.1.1/32 | P2
Solution 2
Solution 1

## Slide 64: Verifying the Configuration (3)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
Check information about routes destined for 10.0.1.1 (PE1) on ASBR-PE2.
<ASBR-PE2>display bgp routing-table 10.0.1.1 32
BGP local router ID : 10.0.4.4
Local AS number : 200
Paths: 1 available, 1 best, 1 select
BGP routing table entry information of 10.0.1.1/32:
Label information (Received/Applied): 1025/NULL
From: 10.0.34.3 (10.0.3.3)
Route Duration: 01h30m31s
Direct Out-interface: GigabitEthernet0/0/1
Relay Tunnel Out-Interface: GigabitEthernet0/0/1
Relay token: 0x1
Original nexthop: 10.0.34.3
Qos information : 0x0
AS-path 100, origin igp, MED 2, pref-val 0, valid, external, best, select, active, pre 255
Based on steps 1 and 3, the packets sent by ASBR-PE2 should carry the following labels:
Label Value | Type | FEC | Label Allocation Device
1028 | VPN label | 192.168.1.0/24 | PE1
1025 | BGP label | 10.0.1.1/32 | ASBR-PE2
Label allocated by ASBR-PE1 to the route destined for 10.0.1.1
Solution 2
Solution 1

## Slide 65: Verifying the Configuration (4)
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
Ping 192.168.1.1 from CE2.
<CE2>ping -a 192.168.2.1 192.168.1.1
PING 192.168.1.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.1.1: bytes=56 Sequence=1 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=2 ttl=250 time=50 ms
Reply from 192.168.1.1: bytes=56 Sequence=3 ttl=250 time=60 ms
Reply from 192.168.1.1: bytes=56 Sequence=4 ttl=250 time=60 ms
Solution 2
Solution 1

## Slide 66: Summary of Key Configurations for Inter-AS VPN Option C (Solution 2)
Device | Key Points
PE1 PE2 | Enable PEs to establish MP-IBGP peer relationships with RRs in the local AS.
RR1 RR2 | Enable RRs to establish MP-EBGP peer relationships with RRs in other ASs and not to change the next hops of routes. Enable RRs to establish MP-IBGP peer relationships with PEs in the same AS and not to change the next hops of routes.
ASBR-PE1 ASBR-PE2 | Enable ASBR-PEs to exchange labeled IPv4 routes with ASBR-PEs in other ASs. Enable ASBR-PEs to establish LDP LSPs for labeled BGP routes of the public network. Enable MPLS on the interfaces connecting ASBRs.
PE1
CE1
PE2
CE2
P1
ASBR-PE1
ASBR-PE2
P2
192.168.1.1/24
192.168.2.1/24
AS100
AS200
GE2/0/0
10.0.34.0/24
RR1
RR2
Solution 2
Solution 1

## Slide 67
(Single-answer question) Which of the following inter-AS VPN solutions does not require ASBRs to save CE-side routing information? ( )
  Option A
  Option B
  Option C
(Single-answer question) When only LDP or BGP is used to allocate labels, which of the following inter-AS VPN solutions may use three types of labels during packet forwarding? ( )
  Option A
  Option B
  Option C
Notes: C
C

## Slide 68
When VPN routing information is exchanged between ASs, three inter-AS VPN solutions are proposed in related standards:
  Option A: It features simple configurations as MPLS does not need to run between ASBRs. It is applicable to the scenario with a small number of VPNs.
  Option B: It does not require interfaces to be created for each inter-AS VPN. All traffic is forwarded by ASBRs, facilitating traffic control but burdening ASBRs. When there are a large number of VPN routes, ASBRs are overloaded and may become a bottleneck.
  Option C: It does not require ASBRs to maintain or advertise VPN-IPv4 routes because these routes are directly exchanged between PEs. Option C is applicable to scenarios where multiple ASs are spanned. The disadvantage of Option C is that it costs too much to manage an end-to-end BGP LSP between PEs.