## Slide 1
Datacom
General
V1.0
He Junjian/WX580230
2021.08.02
Lu Yueyue/WX445705
New

## Slide 2: EVPN Fundamentals and Configuration

## Slide 3
Virtual Private LAN Service (VPLS) is a point-to-multipoint (P2MP) L2VPN service provided over a public network.
VPLS cannot implement load balancing, simplify network deployment, provide flexible L2VPN deployment, or improve link efficiency in CE multi-homing scenarios. Ethernet Virtual Private Network (EVPN) solves these problems.
Defined in RFC7432, EVPN introduces the control plane to control MAC address learning. EVPN has been continuously expanded to support both L2VPN and L3VPN.
EVPN has been widely used in various scenarios, such as WANs, data centers (DCs), and campus networks.
This document describes the background, fundamentals, typical route types, and application scenarios of EVPN.

## Slide 4
On completion of this course, you will be able to:
  Describe the background of EVPN.
  Know how EVPN solves VPLS problems.
  Understand the fundamentals and typical route types of EVPN.
  Describe the fundamentals of inter-AS EVPN.
  Describe the typical application scenarios of EVPN.

## Slide 5
EVPN Background and Terms
EVPN Fundamentals
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 6: VPLS Overview
VPLS is an Ethernet-based L2VPN technology. It provides services similar to LAN services on an MPLS network and allows users to access the network from multiple geographical locations and communicate with each other.
Implementing VPLS involves three steps: creating tunnels and pseudo wires (PWs), creating virtual switch instances (VSIs), and binding PWs and attachment circuits (ACs) to VSIs.
PE1
Enterprise A CE1
Enterprise A CE2
Enterprise B CE3
Enterprise B CE4
192.168.1.1
PE2
192.168.1.2
192.168.2.1
192.168.2.2
CE1 and CE2 of enterprise A belong to the same Layer 2 network.
CE3 and CE4 of enterprise B belong to the same Layer 2 network.

## Slide 7: VPLS Fundamentals: Creating Tunnels and PWs
To implement VPLS, you need to establish a tunnel between PE1 and PE2 and then create PWs to carry services of different enterprise customers.
PE1
Enterprise A CE1
Enterprise A CE2
Enterprise B CE3
Enterprise B CE4
192.168.1.1
PE2
192.168.1.2
192.168.2.1
192.168.2.2
PW A carries enterprise A's services.
PW B carries enterprise B's services.
PW A
PW B
Tunnel
PW A
PW B

## Slide 8: VPLS Fundamentals: Creating VSIs
A VSI is an independent virtual switching unit for each VPLS service. A VSI stores an independent MAC address table, forwards packets, and terminates PWs.
PE1
Enterprise A CE1
Enterprise A CE2
Enterprise B CE3
Enterprise B CE4
192.168.1.1
PE2
192.168.1.2
192.168.2.1
192.168.2.2
VSI B
MAC B
VSI B
MAC B
VSI A
MAC A
VSI A
MAC A

## Slide 9: VPLS Fundamentals: Binding PWs and ACs to VSIs
An attachment circuit (AC) is a link between a CE and a PE. After a PW and an AC are bound to a VSI, the VSI works like a switch. The VSI records the MAC addresses learned by different interfaces and generates MAC address entries.
PE1
Enterprise A CE1
Enterprise A CE2
Enterprise B CE3
Enterprise B CE4
192.168.1.1
PE2
192.168.1.2
192.168.2.1
192.168.2.2
VSI B
MAC B
VSI B
MAC B
PW A
PW B
Bind the AC and PW to the VSI.
AC
Tunnel
PW A
PW B
VSI A
MAC A
VSI A
MAC A
Notes: Common VPLS PW creation modes:
  Static configuration: A large number of manual configurations are required.
  LDP signaling (Martini)
  BGP signaling (Kompella)

## Slide 10: VPLS Packet Forwarding
VPLS emulates a switch. MAC address learning depends on flooding on the data plane without involving the control plane.
The forwarding behavior is determined by examining the MAC address table. If packets match an entry in the MAC address table, packets are forwarded according to the table. Otherwise, packets are flooded for forwarding.
ARP request
DIP 192.168.1.2
SIP 192.168.1.1
DMAC ALL
SMAC 1-1-1
1
CE1 sends an ARP request.
MAC
Outbound Interface
1-1-1
Port1
2
PE1 generates a MAC address entry and floods the received ARP request to all the PWs bound the VSI.
MAC
Outbound Interface
1-1-1
PWA
PE2 receives the ARP request and generates a MAC address entry in the VSI.
ARP request
DIP 192.168.1.2
SIP 192.168.1.1
DMAC ALL
SMAC 1-1-1
4
PE2 forwards the ARP request.
PE1
Enterprise A CE1
Enterprise A CE2
192.168.1.1
PE2
192.168.1.2
VSI A
MAC A
PW A
Access from 192.168.1.1 to 192.168.1.2
Tunnel
PW A
VSI A
MAC A
3

## Slide 11: VPLS Challenge 1: Uneven Load Balancing Due to Single-Active Access
In VPLS, if a ring topology is achieved when a CE is dual-homed to two PEs, the loop-free forwarding path is formed by blocking a port. This is the same as the loop prevention technology (STP) of switches. Therefore, VPLS access works in active/standby mode.
There is only one link between the CE and PE for traffic forwarding, and multiple paths cannot be formed between PEs. As a result, some links may be congested.
CE1
CE2
PE1
PE2
PE3
PE4
P
P
The standby link between the CE and PE does not forward data.
Active
Standby
1
Multiple paths cannot be formed between PEs.
2

## Slide 12: VPLS Challenge 2: Slow Fault Convergence
After detecting a link fault, PE3 sends a MAC Withdraw message to the peer PE, instructing the peer PE to delete the MAC address of PE3. PE4 changes the standby link to the active state. After receiving the Withdraw message, PE1 clears the corresponding MAC address and learn MAC addresses again. The fault convergence time is closely related to the number of MAC addresses.
1
PE3 detects a fault and sends a MAC Withdraw message to instruct PE1 to clear the MAC address of PE3 (within subseconds).
2
The link between PE4 and PE2 becomes the active link.
3
PE1 receives the MAC Withdraw message, clears the corresponding MAC address, and learns MAC addresses again for about 10 seconds.
CE1
CE2
PE1
PE2
PE3
PE4
P
P
Active

## Slide 13: EVPN Overview
EVPN changes the traditional MAC address learning mode on the L2VPN data plane. It introduces the control plane to learn MAC addresses and IP addresses for data forwarding, implementing forwarding-control separation.
EVPN implements active-active, fast convergence, and simplified O&M, resolving typical problems of traditional L2VPNs.
EVPN uses Multiprotocol Border Gateway Protocol (MP-BGP) on the control plane and supports multiple types of tunnels on the data plane, such as MPLS tunnels, GRE tunnels, and Segment Routing over IPv6 (SRv6) tunnels. In this course, MPLS is used as the outer tunnel forwarding technology.
CE1
CE2
PE1
PE3
PE2
PE4
Data plane: Data forwarding paths are formed by IP tunnels or MPLS label forwarding paths. The data plane is only responsible for forwarding data and does not need to broadcast packets to learn MAC addresses.
Control plane: PEs exchange BGP EVPN packets to transmit MAC addresses and IP addresses.
Other advantages of EVPN:
  All-active access of CEs to PEs
  Automatic PE discovery
  Loop prevention
  Broadcast traffic optimization
  Equal-cost multi-path routing (ECMP)
EVPN peer relationship

## Slide 14: EVPN Terms
An Ethernet segment (ES) is a group of Ethernet links that connect a user site (device or network) to a PE. An ES is identified by an Ethernet Segment Identifier (ESI).
An EVPN instance (EVI) identifies an EVPN client.
A MAC-VRF table is a MAC address table that belongs to an EVI on a PE.
A route distinguisher (RD) is the unique identifier of an EVPN and identifies an EVI.
Route targets (RTs) are used to control the import of EVPN routes.
In a CE multi-homing scenario, only the PE that is elected as a designated forwarder (DF) forwards broadcast, unknown unicast, and multicast (BUM) traffic to CEs.
ESI Label is an extended community attribute carried in an EVPN Type 1 route. It implements fast convergence and split horizon in multi-homing scenarios.
BUM labels are carried in EVPN Type 3 routes to forward BUM traffic.
Unicast labels are carried in Type 2 routes to forward unicast traffic.
Notes: For details about the terms, see RFC7432.

## Slide 15: EVPN terms: ES and ESI
ES
An ES is a group of Ethernet links that connect a user site (device or network) to a PE. An ES is identified by an ESI.
An ESI is 10 bytes long and is unique on the entire network.
Dual-homing PEs on the same ES must have the same ESI. For example, PE1 and PE2 must be configured with the same ESI (for example, 1).
CE1
CE2
PE4
PE1
PE3
ES
ESI 1
ESI 1
ESI 2
ESI 2
PE2

## Slide 16: ESI Format
Type 0: The ESI is manually configured by the administrator.
Type 1: If LACP is used between a PE and a CE, the ESI is the CE LACP System MAC address (6 bytes) + CE LACP Port Key (2 bytes) + 0x00 (1 byte).
Type 2: The ESI is automatically generated by MSTP.
Type 3: The ESI is system MAC address plus local discriminator.
Type 4: The ESI is router ID plus local discriminator.
Type 5: The ESI is AS number plus local discriminator.
T ype
(1 byte)
ESI Value
(9 bytes)
[*PE1] interface eth-trunk 10
[*PE1-Eth-Trunk10] esi 0000.1111.2222.1111.1111
<PE1> display bgp evpn all esi
Number of ESI for EVPN address family: 1
ESI IFName/Bridge-domain
0000.1111.2222.1111.1111 Eth-Trunk10
Static ESI configuration example.
View ESI information.
Notes: Currently, ESIs of Type 2, Type 3, Type 4 and Type 5 are not used on Huawei devices.

## Slide 17: Basic EVPN Terms: EVI and MAC-VRF
An EVI identifies an EVPN client.
A MAC-VRF table is a MAC address table that belongs to an EVI on a PE.
EVI 1
MAC-VRF
EVI 2
MAC-VRF
EVI 1 and EVI 2 have independent MAC address tables, which can be used to distinguish different services or customers.
ES
CE1
CE2
PE4
PE1
PE3
ES
ESI 1
ESI 1
ESI 2
ESI 2
PE2

## Slide 18: Basic EVPN Terms: RD and RT
An RD is the unique identifier of an EVPN and identifies an EVI.
RTs are used to label routes to control the import of EVPN routes.
EVI 1(RD 1:1, RT 10:10)
MAC-VRF
EVI 2(RD 2:2, RT 20:20)
MAC-VRF
RD 1:1 identifies EVI 1.
RD 2:2 identifies EVI 2.
ES
CE1
CE2
PE4
PE1
PE3
ES
ESI 1
ESI 1
ESI 2
ESI 2
PE2

## Slide 19
EVPN Background and Terms
EVPN Fundamentals
  EVPN Route Overview and Interaction Process
  EVPN Route Types
  EVPN Access Principles
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 20: EVPN Routes
EVPN defines a new BGP network layer reachability information (NLRI), which is known as EVPN NLRI, to carry all EVPN routes.
EVPN NLRI is carried by MP-BGP. MP-BGP supports multi-protocol extensions. In MP-BGP, the Address Family Identifier (AFI) defining EVPN is 25 and the Subsequent Address Family Identifier (SAFI) is 70.
Route Type
Length
1 byte
1 byte
Variable
Ethernet A-D route
MAC/IP advertisement route
Inclusive multicast route
Ethernet segment route
Route Type Specific
EVPN NLRI format
The Route Type field defines four types of common EVPN routes.

## Slide 21: Functions of Four Types of EVPN Routes
RFC7432 defines four types of EVPN routes: Type 1 to Type 4. With the development of the EVPN protocol, more and more routes are redefined. The following describes four types of EVPN routes.
Route Type | Function | Benefits
(Type 1) Ethernet A-D route | Aliasing MAC address withdrawal in batches All-active indication ESI label advertisement | Loop prevention Fast convergence Load balancing
(Type 2) MAC/IP advertisement route | MAC address learning and advertisement MAC/IP binding MAC address mobility | ARP suppression Host migration
(Type 3) Inclusive multicast route | Auto-discovery of multicast tunnel endpoints & multicast types | BUM traffic forwarding
(Type 4) Ethernet segment route | ES member auto-discovery DF election | Support for both all-active and single-active modes
Notes: Up to now, 11 route types have been defined in the RFC and draft. Type 1 to Type 5 are relatively mature. Type 5 is in the draft phase. Type 6 to Type 11 are used for multicast traffic optimization and are not mature.

## Slide 22: EVPN Working Process
The EVPN process is divided into two phases:
  Startup phase
    EVPN peers exchange EVPN Type 3 routes to establish the BUM traffic forwarding table.
    EVPN peers exchange Type 4 routes to complete ES discovery and DF election (in ES multi-homing scenarios).
    EVPN peers exchange Type 1 routes and ESI labels to implement split horizon and aliasing.
  Traffic forwarding phase: CE-side traffic triggers a PE to advertise the MAC address through a Type 2 route. The route carries assigned label information. The PE then forwards unicast traffic based on the label.
CE1
CE2
PE1
PE3
PE2
PE4
P
P
Aggregated port
BUM traffic forwarding table setup (Type 3)
DF election (Type 4)
ESI label advertisement (Type 1)
EVPN traffic forwarding (Type 2)
Notes: The CE all-active access scenario uses Huawei NE series routers as an example. An Eth-Trunk is configured on CE1 to connect to PE1 and PE2, and an inter-device link aggregation enhanced trunk (E-Trunk) needs to be configured on PE1 and PE2. E-Trunk will not be marked in the following figures.

## Slide 23: EVPN Entry Overview
EVPN maintains three tables to guide traffic forwarding: MAC-VRF table, BUM traffic forwarding table, and ES member table.
  The MAC-VRF table is used to record the forwarding of known unicast traffic.
  The BUM traffic forwarding table is used to guide the forwarding of broadcast, unknown unicast, and multicast traffic.
  The ES member table is used to record information about the PEs that users access.
The following describes the generation process and functions of the three tables.
PE1 is used as an example.
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
MAC-VRF |  |  | 
MAC | ESI | Next hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304

## Slide 24: Creating an EVPN Instance Locally
Create an EVPN instance on each PE and configure an RD and an RT for the instance. EVPN is then activated locally on the PE, and the MAC-VRF table with empty content is generated.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
P
CE2
CE1
MPLS backbone network
Notes: The backbone network consisting of P devices involves only outer tunnel forwarding, which will not be described in later sections.

## Slide 25: BUM Traffic Forwarding Table (1)
Establish peer relationships between the PEs. Take PE1 as an example. It sends Type 3 routes to discover neighbors and allocates labels.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
PE1 Type 3 route
RD = rd1
Label = 101
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 26: BUM Traffic Forwarding Table (2)
PE2, PE3, and PE4 each generate a BUM traffic forwarding table.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE1 Type 3 route
RD = rd1
Label = 101
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 27: BUM Traffic Forwarding Table (3)
In this process, all PEs send Type 3 routes to generate a stable BUM traffic forwarding table.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
PE3 Type 3 route
RD = rd3
Label = 103
PE4 Type 3 route
RD = rd4
Label = 104
PE2 Type 3 route
RD = rd2
Label = 102
PE1 Type 3 route
RD = rd1
Label = 101
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 28: Binding an Interface to an EVPN Instance
A CE is dual-homed to PEs in active-active mode. Bind the interface connecting to the CE to the EVPN instance on each PE. Packets received by the interface are then sent to the EVPN instance.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
CE2
CE1

## Slide 29: Configuring ESIs for PEs' Interfaces Connected to CEs
Configure ESIs for PEs' interfaces connected to CEs. PEs exchange Type 4 routes to advertise ESIs and elect a DF.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
PE2 Type 4 route
RD = rd2
ESI = ESI 1
PE1 Type 4 route
RD = rd1
ESI = ESI 1
PE4 Type 4 route
RD = rd4
ESI = ESI 2
PE3 Type 4 route
RD = rd3
ESI = ESI 2
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 30: DF Election (1)
When a CE is multi-homed to multiple PEs, only one PE forwards BUM traffic to the CE. The process of selecting such a PE is DF election.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 
1 | ESI 1 | PE1 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 
1 | ESI 1 | PE1 | 
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 31: DF Election (2)
PEs use a specific algorithm to elect a DF. In this example, PE2 and PE3 are elected as DFs, and only PE2 and PE3 are allowed to forward BUM traffic to CEs.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 
1 | ESI 1 | PE1 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 
1 | ESI 1 | PE1 | 
Notes: The DF election mode can be set to interface-based or VLAN-based DF election on Huawei devices. By default, interface-based DF election is enabled, which may cause traffic unbalance among multi-homing links. You can configure VLAN-based DF election so that BUM traffic from a PE to a CE can be evenly distributed to multi-homing links based on VLANs.

## Slide 32: ESI Label Distribution: Split Horizon (1)
PEs distribute ESI labels through Type 1 routes. ESI labels are used for split horizon to prevent traffic from an ES from being sent back to the ES.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
Non-DF
Non-DF
DF
DF
PE1 Type 1 route
RD = rd1
ESI = ESI 1
ESI Label = 201
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 
1 | ESI 2 | PE4 | 
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 
1 | ESI 1 | PE1 | 

## Slide 33: ESI Label Distribution: Split Horizon (2)
In this process, all PEs send Type 1 routes to generate a complete ES member table.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
EVI 1
MAC-VRF
EVI 1
MAC-VRF
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201

## Slide 34: Summary of the EVPN Startup Phase
During EVPN startup, the MAC-VRF table, BUM traffic forwarding table, and ES member table are generated. In this case, the MAC-VRF table contains empty entries.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201

## Slide 35: EVPN Traffic Forwarding Phase
The EVPN traffic forwarding phase starts when the CE-side user traffic is initiated.
CE1 and CE2 are unaware of EVPN packet exchange between PEs.
In this example, the service process of CE1 accessing CE2 is as follows:
CE1
CE2
IP: 192.168.1.1
MAC: 1-1-1
IP: 192.168.1.2
MAC: 2-2-2
1
CE1 broadcasts an ARP request to request the MAC address of CE2.
2
CE2 responds with a unicast ARP reply.
3
CE1 forwards traffic to CE2.

## Slide 36: Local MAC Address Learning
CE1 sends an ARP request to access CE2. PE1 receives the packet and generates a local MAC address entry.
PE1
PE2
PE3
PE4
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
Non-DF
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Port 1
Port 2
Port 3
Port 4
ARP request
DMAC All
SMAC 1-1-1
ESI 1
ESI 2
ESI 1
ESI 2
CE2
CE1
Notes: The data packets sent by the CEs do not carry any label. Therefore, the incoming label in the MAC-VRF table of PEs is NULL.

## Slide 37: MAC Address Advertisement (1)
PE1 EVPN generates a Type 2 route based on the local MAC address entry, carrying label 301 assigned by PE1.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
Non-DF
DF
DF
Port 1
Port 2
Port 3
Port 4
ARP request
DMAC All
SMAC 1-1-1
PE1 Type 2 route
RD = rd1
ESI = ESI 1
MAC = 1-1-1
MPLS Label = 301
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Non-DF
ESI 1
ESI 2
ESI 1
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 38: MAC Address Advertisement (2)
The peer PE learns the EVPN route through MP-BGP and generates a MAC address entry.
PE1
PE2
PE3
PE4
EVI 1
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Port 1
Port 2
Port 3
Port 4
ARP request
DMAC All
SMAC 1-1-1
PE1 Type 2 route
RD = rd1
ESI = ESI 1
MAC = 1-1-1
MPLS Label = 301
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
EVI 1
ESI 1
ESI 2
ESI 1
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 39: MAC Address Advertisement (3)
EVPN allows CEs to access PEs in all-active mode. PE2 detects that it is directly connected to CE1, updates the optimal MAC address entry, and generates and advertises a Type 2 route.
PE1
PE2
PE3
PE4
EVI 1
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Port 1
Port 2
Port 3
Port 4
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
EVI 1
PE2 Type 2 route
RD = rd2
ESI = ESI 1
MAC = 1-1-1
MPLS Label = 302
ARP request
DMAC All
SMAC 1-1-1
ESI 1
ESI 2
ESI 1
ESI 2
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 40: Remote MAC Address Learning
Because PE1 and PE2 allocate different MPLS labels, PE3 and PE4 each will have two paths to CE1.
PE1
PE2
PE3
PE4
EVI 1
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Port 1
Port 2
Port 3
Port 4
ESI 1
ESI 2
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
EVI 1
ARP request
DMAC All
SMAC 1-1-1
ESI 1
ESI 2
PE2 Type 2 route
RD = rd2
ESI = ESI 1
MAC = 1-1-1
MPLS Label = 302
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 41: ARP Broadcast Forwarding
The ARP request sent by CE1 reaches PE1. PE1 learns the MAC address of CE1 through the data plane and sends the MAC address to all neighbors through a Type 2 route.
After the control plane behavior is completed, PE1 performs the data plane behavior, that is, forwards the ARP broadcast request. Because PE3 is the DF, it forwards the ARP broadcast packet to CE2.
CE1
CE2
PE1
PE3
PE2
PE4
1
The control plane of PE1 advertises the MAC address.
2
The data plane of PE1 forwards the ARP packet.
ARP broadcast
DF
3
PE3 forwards the ARP packet.

## Slide 42: ARP Broadcast Forwarding: from PE1 to PE3
The ARP packet carrying label 103 from PE1 to PE3 is forwarded based on the BUM traffic forwarding table. PE3 functions as the DF and forwards the packet through Port3.
ARP request
DMAC All
SMAC 1-1-1
ARP request
DMAC All
SMAC 1-1-1
103
Tunnel
ARP request
DMAC All
SMAC 1-1-1
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
Notes: PE1 forwards the ARP packet to all members based on the BUM traffic forwarding table.

## Slide 43: ARP Broadcast Forwarding: from PE1 to PE4
Traffic from PE1 to PE4 carries label 104. PE4 determines that the traffic is BUM traffic based on the label and discards the traffic because PE4 is a non-DF.
ARP request
DMAC All
SMAC 1-1-1
ARP request
DMAC All
SMAC 1-1-1
104
Tunnel
ARP request
DMAC All
SMAC 1-1-1
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
Notes: Only the router that is elected as the DF forwards BUM traffic to CEs.

## Slide 44: ARP Broadcast Forwarding: from PE1 to PE2
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
Because PE1 and PE2 belong to the same ES, traffic from PE1 to PE2 carries both the ESI label 202 and the BUM label 102. After receiving the packet, PE2 finds that the packet carrying the label 202 and discards the packet.
ARP request
DMAC All
SMAC 1-1-1
ARP request
DMAC All
SMAC 1-1-1
202
102
Tunnel
ARP request
DMAC All
SMAC 1-1-1
Split horizon is implemented using the ESI labels assigned to Type 1 routes.
PE1
PE2
PE3
PE4
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
MAC-VRF
EVI 1
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE2 | 102
PE3 | 103
BUM traffic forwarding table | 
Peer | Label
PE1 | 101
PE3 | 103
PE4 | 104
BUM traffic forwarding table | 
Peer | Label
PE2 | 102
PE3 | 103
PE4 | 104
Non-DF
Non-DF
DF
DF
ESI 1
ESI 1
ESI 2
ESI 2
CE2
CE1
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
Notes: ESI labels are used to prevent CE traffic from being looped back.

## Slide 45: Unicast ARP Reply
CE2 sends a unicast ARP reply. PE3 learns the MAC address of CE2 and sends a Type 2 route to trigger the EVPN control plane behavior. PE3 searches the MAC address table to forward the unicast ARP packet to PE1. Finally, PE1 forwards the ARP packet to CE1.
1
CE2 sends an ARP reply.
2
PE3 learns the MAC address of CE2 and triggers MAC address learning on the EVPN control plane.
CE1
CE2
PE1
PE3
PE2
PE4
Unicast ARP reply
3
PE3 forwards the ARP packet on the data plane.
4
PE1 forwards the ARP packet.

## Slide 46: Unicast ARP Reply: Local MAC Address Learning
CE2 sends a unicast ARP reply. PE3 learns the MAC address of CE2 through the data plane and generates a local MAC-VRF entry.
PE1
PE2
PE3
PE4
EVI 1
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
Port 1
Port 2
Port 3
Port 4
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
EVI 1
ESI 1
ESI 2
ESI 1
ESI 2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
CE2
CE1

## Slide 47: Unicast ARP Reply: MAC Address Advertisement (1)
PE3 generates and advertises a Type 2 route. After receiving the Type 2 route, the other PEs update their local MAC address entries.
PE1
PE2
PE3
PE4
EVI 1
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
Port 1
Port 2
Port 3
Port 4
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
2-2-2 | ESI 2 | PE3 | 303
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | PE3 | 303
EVI 1
ESI 1
ESI 2
ESI 1
ESI 2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
RD = rd3
ESI = ESI 2
MAC = 2-2-2
MPLS Label = 303
PE3 Type 2 route
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 48: Unicast ARP Reply: MAC Address Advertisement (2)
The interface of PE4 belongs to ESI 2, so PE4 updates its MAC address table, and generates as well as advertises a Type 2 route.
PE1
PE2
PE3
PE4
Non-DF
DF
DF
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
Port 1
Port 2
Port 3
Port 4
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
EVI 1
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
EVI 1
ESI 1
ESI 2
ESI 1
ESI 2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
RD = rd4
ESI = ESI 2
MAC = 2-2-2
MPLS Label = 304
PE4 Type 2 route
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 4 | NULL
CE2
CE1
Type 4 Route
Type 1 Route
Type 2 Route
Type 3 Route

## Slide 49: Unicast ARP Reply: Data Plane Forwarding
PE3 uses a load balancing algorithm to find a next hop (for example, PE1) for sending packets carrying label 301. After receiving the packet, PE1 forwards the packet through Port1.
PE1
PE2
PE3
PE4
Non-DF
DF
DF
Port 1
Port 2
Port 3
Port 4
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 4 | NULL
EVI 1
ESI 1
ESI 2
ESI 1
ESI 2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
ARP reply
DMAC 1-1-1
SMAC 2-2-2
301
Tunnel
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
EVI 1
EVI 1
CE2
CE1
Notes: PE3 searches the MAC-VRF table based on the destination MAC address (1-1-1) of the packet and finds that there are two next hops: PE1 and PE2. PE3 uses a load balancing algorithm to select an appropriate next hop (for example, PE1) for packet forwarding.
After receiving the ARP reply, PE1 searches the MAC-VRF table and sends the packet through Port1.

## Slide 50: Summary: EVPN Solves the Problems Brought by the Active-Active Mode
PE1
PE2
PE3
PE4
Non-DF
DF
DF
Port 1
Port 2
Port 3
Port 4
Non-DF
ESI 1
ESI 2
ESI 1
ESI 2
CE2
CE1
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 2 | PE3 | 203
1 | ESI 2 | PE4 | 204
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ES member table |  |  | 
No. | ESI | Member | Label
0 | ESI 1 | PE2 | 202
1 | ESI 1 | PE1 | 201
ESIs carried in Type 1 routes prevent loops on the CE side. Type 4 routes are used for DF election, preventing multiple copies of broadcast traffic from being sent to CEs.
BUM Traffic

## Slide 51: Summary: EVPN Implements Load Balancing
Data 3
EVPN implements full-path load balancing.
Data 1
Data 2
Data 3
Data 4
Data 1
Data 2
Data 4
PE1
PE2
PE3
PE4
Non-DF
DF
DF
Non-DF
CE2
CE1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 4 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
EVI 1
EVI 1
EVI 1
EVI 1
Notes: CE1 sends traffic to PE1 and PE2 over two active paths for load balancing. Because PE1 and PE2 each have established two paths to CE2, traffic can be load balanced between the two paths. Finally, four service data flows are sent to CE2 over different paths.

## Slide 52: Summary: EVPN Achieves Fast Convergence
After detecting a link fault on CE2, PE3 deletes the local MAC address entry and sends a Type 1 route to instruct other PEs to withdraw all the MAC addresses associated with an ES.
PE1
PE2
PE3
PE4
Non-DF
DF
DF
Non-DF
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 3 | NULL
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | PE1 | 301
1-1-1 | ESI 1 | PE2 | 302
2-2-2 | ESI 2 | Port 4 | NULL
EVI 1
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port1 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
MAC-VRF |  |  | 
MAC | ESI | Next Hop | Label
1-1-1 | ESI 1 | Port2 | NULL
2-2-2 | ESI 2 | PE3 | 303
2-2-2 | ESI 2 | PE4 | 304
EVI 1
EVI 1
RD = rd3
ESI = ESI 2
PE3 Type 1 route
become the DF
CE2
CE1
Notes: After receiving the Type 1 route, PE4 becomes a DF.
After receiving the Type 1 route, PE1 and PE2 update their MAC labels and withdraw the MAC routes to ES2. Traffic is automatically switched to PE4.
If a CE is connected to multiple PEs and a connectivity fault occurs between a specific PE and the CE, the PE must send an Ethernet A-D per ES route to withdraw all the MAC addresses previously advertised.

## Slide 53
EVPN Background and Terms
EVPN Fundamentals
  EVPN Route Overview and Interaction Process
  EVPN Route Types
  EVPN Access Principles
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 54: EVPN Route Review
The EVPN working process describes the functions of Type 1 to Type 4 routes. This section will continue to describe the packets and application scenarios of EVPN routes.
Route Type | Function | Benefits
(Type 1) Ethernet A-D route | Aliasing MAC address withdrawal in batches All-active indication ESI label advertisement | Loop prevention Fast convergence Load balancing
(Type 2) MAC/IP advertisement route | MAC address learning and advertisement MAC/IP binding MAC address mobility | Policy based on each MAC address ARP suppression Host migration
(Type 3) Inclusive multicast route | Auto-discovery of multicast tunnel endpoints & multicast types | BUM traffic forwarding
(Type 4) Ethernet segment route | ES member auto-discovery DF election | Support for both all-active and single-active modes

## Slide 55: Key Parameters Carried in EVPN Routes
The functions of the four types of EVPN routes are closely related to the parameters carried in the routes.
  Type 1 routes carry ESI labels to implement split horizon.
  Type 2 routes carry unicast labels to guide unicast traffic forwarding.
  Type 3 routes carry BUM labels to guide BUM traffic forwarding, but Type 3 routes do not carry ES information.
  Type 4 routes carry ESIs for DF election but do not carry any label information.
Parameter Route Type | RD | ESI | Ethernet Tag ID | Originating Router's IP Address | MAC/IP Address | MPLS Label
Type 1 | √ | √ | √ |  |  | ESI Label
Type 2 | √ | √ | √ |  | √ | √
Type 3 | √ |  | √ | √ |  | BUM Label
Type 4 | √ | √ |  | √ |  | 

## Slide 56: Ethernet A-D Route
Ethernet Auto-Discovery (A-D) routes are classified into two types:
  Ethernet A-D per ES route: used for fast convergence, redundancy mode, and split horizon.
  Ethernet A-D per EVI route: used for aliasing.
NLRI Format | Field Description
Route Distinguisher (8 bytes) | In an Ethernet A-D per ES route, this field contains the source IP address configured on a PE, for example, X.X.X.X:0. In an Ethernet A-D per EVI route, this field is the RD of an EVPN instance.
Ethernet Segment Identifier (10 bytes) | This field uniquely identifies connections between PEs and a CE. In an Ethernet A-D per ES route, this field is all Fs. In an Ethernet A-D per EVI route, this field identifies different sub-broadcast domains of an ES. If this field is all 0s, the EVI has only one broadcast domain.
Ethernet Tag ID (4 bytes) | This field identifies an Ethernet tag. According to the RFC recommendation, the last 20 bits of this field can be the VLAN ID.
MPLS Label (3 bytes) | In an Ethernet A-D per ES route, the field is all 0s. In an Ethernet A-D per EVI route, this field is the MPLS label used to forward EVPN unicast traffic in load balancing mode.
Type 2
Type 4
Type 3
Type 1

## Slide 57: ESI Label Extended Community Attribute
ESI Label is an extended community attribute carried in an EVPN Type 1 route.
In a multi-homing scenario, Type 1 routes must carry this community attribute to implement split horizon.
Extended Community Attribute | Field Description
Type (1 byte) | This field has a fixed value of 0x06.
Sub-Type (1 byte) | This field has a fixed value of 0x01.
Flag (1 byte) | The lowest bit of this field is defined as the single-active bit. The value 0 indicates the multi-active scenario.
Reserved (2 bytes) | This field is reserved and all 0s.
ESI Label (3 bytes) | This field is used by a PE to identify each ES for split horizon.
Type 2
Type 4
Type 3
Type 1

## Slide 58: Fast Convergence
In EVPN, MAC address learning is controlled by BGP. On a large-scale complex network, route convergence takes a long time. To address this issue, EVPN defines a mechanism to efficiently instruct peer PEs to update their forwarding tables. Specifically, PEs advertise Ethernet A-D per ES routes for all ESs.
When a PE detects a fault on the connected CE, the PE withdraws the corresponding MAC address entry and sends an Ethernet A-D per ES route to instruct other PEs to withdraw the corresponding MAC address entry.
An Ethernet A-D per ES route must carry the ESI Label extended community attribute.
PE1
PE2
PE3
ES1
ES1
CE1
Site 1
CE2
Site 2
BGP Update message: Ethernet A-D per ES route
Type 2
Type 4
Type 3
Type 1

## Slide 59: Split Horizon
When a CE is multi-homed to PEs, if the links of the CE work in all-active mode, BUM packets sent by the CE to a PE may be looped back by another PE. This problem needs to be solved using split horizon.
All PEs advertise Ethernet A-D per ES routes that carry the ESI Label extended community attribute to implement split horizon. As shown in the following figure, PE2 (DF) assigns an ESI label to identify ES1 and advertises the label to PE1 (non-DF) through an Ethernet A-D per ES route. PE1 adds this label to a BUM packet before sending the packet to PE2. After receiving the packet, PE2 finds that the label is assigned by itself and does not forward the packet to ES1.
PE1
PE2
DF
PE3
ES1
ES1
CE1
Site 1
CE2
Site 2
BUM
Type 2
Type 4
Type 3
Type 1
1
PE2 allocates an MPLS label, for example, Label1, to ES1.
2
When sending BUM traffic to PE2, PE1 adds Label1 and then the BUM label assigned by PE2 to the traffic.
Before sending BUM traffic to PE3, PE1 adds the BUM label assigned by PE3 to the traffic.
PE2 identifies Label1 and does not forward the BUM traffic to CE1, but sends the traffic to other ESs in the EVPN instance.
3
4
PE3 forwards the BUM traffic to CE2.

## Slide 60: Aliasing
When a CE is multi-homed to PEs in all-active mode, some PEs may fail to learn the MAC address of the CE. As a result, the peer PE receives MAC/IP advertisement routes from only one PE, failing to implement load balancing among paths between PEs. Aliasing solves this problem using Ethernet A-D per EVI routes. Aliasing ensures that a PE is reachable even if the PE does not learn MAC addresses from the EVI/ES.
In this example, CE1 is dual-homed to PE1 and PE2. If PE1 has learned the address of Site1 but PE2 has not, PE1 sends a MAC/IP route carrying detailed information to PE2, and PE2 advertises reachability through an Ethernet A-D per EVI route. Therefore, PE3 considers that PE1 and PE2 at Site 1 are reachable.
PE1
PE2
PE3
ES1
ES1
CE1
Site 1
CE2
Site 2
BGP Update message: MAC/IP advertisement route
BGP Update message: Ethernet A-D per EVI route
Advertise routes destined for Site 1.
Advertise the reachability to Site 1.
Type 2
Type 4
Type 3
Type 1
Notes: When a peer PE receives a MAC/IP advertisement route, it needs to check whether the advertised MAC address is reachable through other PEs. Therefore, the PE checks the address reachability based on the Ethernet A-D per EVI route.
Note: The peer PE may first receive the Ethernet A-D per EVI route and then the Ethernet A-D per ES route. To prevent this problem, the peer PE forwards traffic only when it receives the Ethernet A-D per EVI route and Ethernet A-D per ES route at the same time.
When a CE is multi-homed to PEs in single-active mode, the PE establishes a backup path using the Ethernet A-D per EVI route and Ethernet A-D per ES route.

## Slide 61: MAC/IP Advertisement Route
MAC/IP advertisement routes are used to advertise MAC and IP addresses.
NLRI Format | Field Description
Route Distinguisher (8 bytes) | This field indicates the RD of an EVPN instance.
Ethernet Segment Identifier (10 bytes) | This field uniquely identifies connections between PEs and a CE.
Ethernet Tag ID (4 bytes) | This field is the VLAN ID configured on the device.
MAC Address Length (1 byte) | This field is set to 48 bits.
MAC Address (6 bytes) | This field indicates the host MAC address carried in the route.
IP Address Length (1 byte) | This field is optional and can be set to 32 or 128 bits.
IP Address (0, 4, or 16 bytes) | This field is optional and indicates the host IP address carried in the route.
MPLS Label1 (3 bytes) | This field is assigned by the downstream router to forward Layer 2 service traffic.
MPLS Label2 (0 or 3 bytes) | This field is optional and used to forward Layer 3 service traffic.
Type 2
Type 4
Type 3
Type 1

## Slide 62: MAC Mobility Extended Community Attribute
MAC Mobility is an extended community attribute carried in an EVPN Type 2 route.
The least significant bit in the Flag field is defined as the Sticky/static bit. If this bit is 1, the MAC address is fixed and cannot be moved.
Extended Community Attribute | Field Description
Type (1 byte) | This field has a fixed value of 0x06.
Sub-Type (1 byte) | This field has a fixed value of 0x00.
Flag (1 byte) | The least significant bit of this field is defined as the Sticky/static bit. If this bit is 0, the MAC address can be moved.
Reserved (1 byte) | This field is reserved and all 0s.
Sequence Number (4 bytes) | This field ensures that a PE has correct MAC/IP advertisement routes when multiple update messages are received.
Type 2
Type 4
Type 3
Type 1
Notes: MAC address migration will be described based on VXLAN in the following sections.

## Slide 63: Inclusive Multicast Route
Inclusive multicast routes are used to process BUM traffic. BUM traffic includes broadcast, multicast, and unknown unicast traffic.
After a BGP peer relationship is established between PEs, the PEs transmit inclusive multicast routes to each other. An inclusive multicast route carries the RD and RTs of the EVPN instance on the local PE, source IP address (usually the loopback address of the local PE), and Provider Multicast Service Interface (PMSI). The PMSI and RT are carried in route attribute information while the RD and source IP address are carried in NLRI information.
NLRI Format | Field Description
Route Distinguisher (8 bytes) | This field indicates the RD of an EVPN instance.
Ethernet Tag ID (4 bytes) | This field is the VLAN ID configured on the device.
IP Address Length (1 byte) | This field indicates the length of the source IP address configured on a PE.
Originating Router's IP Address (4 or 16 bytes) | This field indicates the source IP address configured on a PE.
Type 2
Type 4
Type 3
Type 1

## Slide 64: PMSI Attribute
The PMSI attribute carries the tunnel type (ingress replication or MLDP) and tunnel label information used for transmitting multicast packets.
A PE forwards the multicast traffic that it receives to other PEs in P2MP mode. The PEs can establish a tunnel to transmit multicast traffic through inclusive multicast routes.
The PMSI attribute is defined in RFC6514. In the EVPN scenario, the Leaf bit in the Flags field is 0 and the tunnel type is 6 (ingress replication).
PMSI Attribute | Field Description
Flags (1 byte) | The last bit of this field is the Leaf bit.
Tunnel Type (1 byte) | The value of this field is typically 6 (ingress replication) in EVPN.
MPLS Label (3 bytes) | This field is an MPLS label.
Tunnel Identifier (variable length) | This field is the IP address of the tunnel end.
Type 2
Type 4
Type 3
Type 1

## Slide 65: Ethernet Segment Route
Ethernet segment routes are mainly used for DF election.
Ethernet segment routes carry the ESI, source IP address, and RD (source IP address:0) of the local PE. PEs connecting to the same CE use Ethernet segment routes to discover each other.
NLRI Format | Field Description
Route Distinguisher (8 bytes) | This field indicates the RD of an EVPN instance.
Ethernet Segment Identifier (10 bytes) | This field is the unique identifier of the connection between local and peer devices.
IP Address Length (1 byte) | This field indicates the IP address length.
Originating Router's IP Address (4 or 16 bytes) | This field indicates the source address configured on a PE.
Type 2
Type 4
Type 3
Type 1

## Slide 66: ES-Import Route Target
ES-Import RT is an extended community attribute newly defined in EVPN and carried in Type 4 routes.
In an EVPN multi-homing scenario, the ES routes advertised by BGP EVPN must carry the ES-Import RT attribute for ES route filtering.
ES route filtering: ES-Import RT allows only PEs connected to the same site to import Type 4 routes. RTs are used to import Ethernet segment routes to all the PEs connected to the same site.
Extended Community Attribute | Field Description
Type (1 byte) | This field has a fixed value of 0x06.
Sub-Type (1 byte) | This field has a fixed value of 0x02.
ES-Import (2 bytes) | The least significant bit of this field is defined as the Single-Active bit. The value 0 indicates the multi-homing scenario.
ES-Import Cont'd (4 bytes) | This field is reserved and all 0s.
Type 2
Type 4
Type 3
Type 1

## Slide 67: DF Election
In a CE multi-homing scenario, an ES may be configured with multiple Ethernet tags, and only one PE is elected as a designated forwarder (DF). DF election is implemented using Type 4 routes that carry the ES-Import attribute. A DF provides the following functions:
  Sends multicast and broadcast traffic to the CEs on the specified ES.
  Floods unknown unicast traffic to CEs.
PE1
PE2
PE3
ES1
ES1
CE1
Site 1
CE2
Site 2
BUM
DF
non-DF
Type 2
Type 4
Type 3
Type 1
Notes: DF election rules:
  A PE discovers the ES and ESI of the local connection and advertises the Type 4 route carrying the ES-Import.
  The PE starts the timer. The default value of the timer is 3 seconds, within which ES routes can be received.
  After the timeout, the PE generates an ordered list. The list contains the IP addresses of all PEs and information about their connections to the ES. The sequence number of the list starts from 0 in ascending order. The sequence number is used to determine the DF.
  The PE elected as the DF forwards BUM traffic to CEs. When a link fault occurs, the PE withdraws its ES routes, which triggers a re-election process.

## Slide 68: New EVPN Routes
EVPN is not limited to L2VPN applications. With the increase of EVPN route types, more applications, such as L3VPN, are supported.
Route Type | Function | Benefits
(Type 1) Ethernet A-D route | Aliasing MAC address withdrawal in batches All-active indication ESI label advertisement | Loop prevention Fast convergence Load balancing
(Type 2) MAC/IP advertisement route | MAC address learning and advertisement MAC/IP binding MAC address mobility | Policy based on each MAC address ARP suppression Host migration
(Type 3) Inclusive multicast route | Auto-discovery of multicast tunnel endpoints & multicast types | BUM traffic forwarding
(Type 4) Ethernet segment route | ES member auto-discovery DF election | Support for both all-active and single-active modes
(Type 5) IP prefix route | IP prefix advertisement | Support for L3VPN

## Slide 69: IP Prefix Route
IP prefix routes are used to advertise a host IP address received from an access network or the network segment where the host IP address resides.
NLRI Format | Field Description
Route Distinguisher (8 bytes) | This field indicates the RD of an EVPN instance.
Ethernet Segment Identifier (10 bytes) | This field uniquely identifies connections between PEs and a CE.
Ethernet Tag ID (4 bytes) | Currently, this field can only be set to 0.
IP Prefix Length (1 byte) | This field indicates the mask length of the IP prefix carried in the route.
IP Prefix (4 or 16 bytes) | This field indicates the IP prefix carried in the route.
GW IP Address (4 or 16 bytes) | This field indicates the default gateway address.
MPLS Label (3 bytes) | This field indicates the label used for Layer 3 service traffic forwarding.
Notes: For more details about Type 5 routes, see the RFC draft.

## Slide 70: Typical Application Scenarios of IP Prefix Routes
Type 5 routes are advertised to an EVPN instance to implement interworking between the EVPN instance and external networks.
PE1
PE2
Type 5 route
RD = 100:1
Network segment: 10.0.0.0/8
BGP Update message
RT: 10:10
10.0.0.0/8
EVI: RD 100:1 RT 10:10
EVPN peer

## Slide 71: EVPN Protocol Standards
Control
plane
RFC 7432
BGP MPLS-Based Ethernet VPN
RFC 8365
A Network Virtualization Overlay Solution using EVPN
draft-ietf-bess-evpn-inter-subnet-forwarding
Integrated Routing and Bridging in EVPN
IP Prefix Advertisement in EVPN
draft-ietf-bess-evpn-prefix-advertisement
Data
plane
RFC 7348
(Virtual eXtensible Local Area Network)
VXLAN (IP overlay)
MPLS
RFC 7432
(BGP MPLS-Based Ethernet VPN)

## Slide 72
EVPN Background and Terms
EVPN Fundamentals
  EVPN Route Overview and Interaction Process
  EVPN Route Types
  EVPN Access Principles
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 73: EVPN Access Overview
Multiple Ethernet VPN instances (EVIs) can be configured on PEs at the edge of an EVPN, with each EVI connecting to one or more user networks. EVPN allows user network access in various service modes, as described in the following table.
Service Mode | Application Scenario
Port-based mode | The physical interface connected to a user network is directly bound to a common EVI. This service mode is used to carry only Layer 2 services.
VLAN-based mode | The physical interface connected to a user network is divided into different sub-interfaces. Each sub-interface is bound to a specific EVI. One EVI is required per user. This service mode is used to carry Layer 2 or Layer 3 services.
VLAN bundle mode | Users are divided based on VLANs. Each VLAN is bound to a specific EVI. This service mode is used to carry Layer 2 or Layer 3 services.
VLAN-aware bundle mode | Users are divided based on VLANs. The VLANs are bound to the same EVI. This service mode is used to carry Layer 2 or Layer 3 services.

## Slide 74: Port-based Mode
In port-based mode, an interface is used only by a single user. Specifically, the physical interface connected to a user network is bound to a common EVI and has no sub-interfaces created. This service mode is used only to carry Layer 2 services.
PE
GE1/0/0
[~PE] interface GigabitEthernet 1/0/0
[*PE-GigabitEthernet1/0/0] evpn binding vpn-instance evpna
[*PE-GigabitEthernet1/0/0] commit
[~PE-GigabitEthernet1/0/0] quit
EVPN A

## Slide 75: VLAN-based Mode
In VLAN-based mode, the physical interfaces connected to user networks each have different sub-interfaces created. Each sub-interface is associated with a unique VLAN and added to a specific BD, and each BD is bound to a specific EVI. This service mode is used to carry Layer 2 or Layer 3 services. In this example, User1 and User2 access the network through different sub-interfaces.
PE
EVPN A configuration example:
[~PE] bridge-domain 10
[*PE-bd10] evpn binding vpn-instance evpna
[*PE-bd10] quit
[*PE] interface GigabitEthernet 1/0/0.1 mode l2
[*PE-G1/0/0.1] encapsulation dot1q vid 10
[*PE-G1/0/0.1] bridge-domain 10
[*PE-G1/0/0.1] commit
BD 10
GE1/0/0.1
GE1/0/0.2
EVPN A
BD 20
EVPN B
VLAN 10
User1
User2
User1's service packets are tagged with VLAN 10 and transmitted through GE1/0/0.1.
User2's service packets are tagged with VLAN 20 and transmitted through GE1/0/0.2.
VLAN 20
Notes: In this service mode, the sub-interface, VLAN, BD, and EVI are exclusively used by a user to access the network, and a separate MAC forwarding table is used on the forwarding plane for each user. Although this mode effectively ensures service isolation, it consumes a large amount of EVI resources because each user requires one EVI.

## Slide 76: VLAN Bundle Mode
In VLAN bundle mode, an EVI connects to multiple users who are divided by VLAN, and the EVI is bound to a BD. In this service mode, the users connected to the same EVI share a MAC forwarding table, requiring each user on the network to have a unique MAC address. This service mode is used to carry Layer 2 or Layer 3 services.
EVPN A configuration example:
[~PE] bridge-domain 10
[*PE-bd10] evpn binding vpn-instance evpna
[*PE-bd10] quit
[*PE] interface GigabitEthernet 1/0/0.1 mode l2
[*PE-G1/0/0.1] encapsulation dot1q vid 10
[*PE-G1/0/0.1] bridge-domain 10
[*PE-G1/0/0.1] commit
PE
GE1/0/0.1
GE1/0/0.2
EVPN A
VLAN 10
User1
User2
User1's service packets are tagged with VLAN 10 and transmitted through GE1/0/0.1.
User2's service packets are tagged with VLAN 20 and transmitted through GE1/0/0.2.
VLAN 20
BD 10

## Slide 77: VLAN-Aware Bundle Mode
In VLAN-aware bundle mode, an EVI connects to multiple users divided by VLAN. Additionally, the EVI can be bound to multiple BDs. In this service mode, users connected to the same EVI use separate forwarding entries. During traffic forwarding, the system uses the BD tag carried in packets to locate the corresponding BD MAC forwarding table and searches the table for a forwarding entry based on a MAC address.
EVPN A configuration example:
[~PE] bridge-domain 10
[*PE-bd10] evpn binding vpn-instance evpna bd-tag 10
[*PE-bd10] quit
[*PE] interface GigabitEthernet 1/0/0.1 mode l2
[*PE-G1/0/0.1] encapsulation dot1q vid 10
[*PE-G1/0/0.1] bridge-domain 10
[*PE-G1/0/0.1] commit
PE
GE1/0/0.1
GE1/0/0.2
EVPN A
VLAN 10
User1
User2
User1's service packets are tagged with VLAN 10 and transmitted through GE1/0/0.1.
User2's service packets are tagged with VLAN 20 and transmitted through GE1/0/0.2.
VLAN 20
BD 10
BD 20
Notes: When EVPN peers send routes to each other, a BD tag is encapsulated into the Ethernet Tag ID field of Ethernet A-D route packets, MAC/IP advertisement route packets, and inclusive multicast route packets.

## Slide 78
EVPN Background and Terms
EVPN Fundamentals
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 79: Inter-AS EVPN Overview
Typically, an EVPN architecture runs in an autonomous system (AS). Routing information of any EVPN can be flooded only in the local AS. In some complex scenarios, an enterprise may have multiple ASs. In this case, the existing EVPN architecture needs to be extended to provide an inter-AS EVPN.
Inter-AS EVPN can be implemented in the following ways, similar to inter-AS MPLS VPN:
  Option A
  Option B
  Option C
Notes: This course describes inter-AS EVPN L3VPN.

## Slide 80: Inter-AS EVPN: Option A
In inter-AS EVPN Option A, EVPN peer relationships need to be established between PEs and ASBRs, and EVPN does not need to run between ASBRs.
Multiple sub-interfaces are created between ASBRs and bound to VPN instances to transmit IP routes.
In Option A, intra-AS traffic has two labels, and inter-AS traffic has no label.
PE1
ASBR2
ASBR1
CE1
PE2
CE2
AS1
AS2
IP
Eth
IP
Eth
EVPN Label
Tunnel Label
Eth
IP
Eth
IP
Eth
IP
Eth
EVPN Label
Tunnel Label
Eth
EVPN
EVPN

## Slide 81: Inter-AS EVPN: Option B
In inter-AS EVPN Option B, EVPN peer relationships need to be established between PEs and ASBRs, and between ASBRs.
After receiving a MAC/IP advertisement route, an ASBR changes the next hop to itself, allocates a new label to the route, and sends the route to the ASBR in another AS.
In Option B, intra-AS traffic has two labels, and inter-AS traffic has one label (EVPN label).
IP
Eth
IP
Eth
EVPN Label 1
Tunnel Label
Eth
IP
Eth
EVPN Label 2
Eth
IP
Eth
IP
Eth
EVPN Label 3
Tunnel Label
Eth
PE1
ASBR2
ASBR1
Site 1
PE2
Site 2
AS1
AS2
EVPN
EVPN
EVPN

## Slide 82: Inter-AS EVPN: Option C
In inter-AS EVPN Option C, an E2E BGP LSP needs to be established between the PEs at different sites (Site 1 and Site 2 in this example).
PE1 and PE2 establish an EVPN peer relationship. ASBRs are unaware of MAC/IP advertisement routes.
In Option C, intra-AS traffic has three labels, and inter-AS traffic has two labels (EVPN label and BGP label).
PE1
ASBR2
ASBR1
Site 1
PE2
Site 2
AS1
AS2
IP
Eth
IP
Eth
EVPN Label
BGP Label 1
Tunnel Label
Eth
IP
Eth
EVPN Label
BGP Label 2
Eth
IP
Eth
IP
Eth
EVPN Label
BGP Label 3
Tunnel Label
Eth
EVPN
IBGP
EBGP
IBGP

## Slide 83
EVPN Background and Terms
EVPN Fundamentals
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations

## Slide 84: EVPN Application on a WAN
E-LAN | E-Line | E-Tree | L3VPN
VPWS
VPLS
VPLS
ETREE
EVPN
PBB-EVPN
EVPN
VPWS
EVPN
ETREE
Without EVPN
With EVPN
RFC7432
Basic Standard
RFC7623
RFC8214
RFC8317
L3VPN
EVPN
L3VPN
draft-ietf-bess-evpn-prefix-advertisement-11
Notes: E-Line, E-Tree, and E-LAN are three types of Ethernet virtual connection (EVC), which are point-to-point EVC, multipoint-to-multipoint EVC, and rooted-multipoint EVC.
  E-Line: A point-to-point EVC associates two user-network interfaces (UNIs).
  E-LAN: A multipoint-to-multipoint EVC can associate two or more UNIs. Users or carriers can add any number of UNIs to the EVC or delete some UNIs from the EVC without affecting other UNIs.
  E-Tree: This EVC is similar to the hub-spoke model in L3VPN. It consists of one or more root UNIs and several leaf UNIs. The root UNI can directly communicate with all UNIs in the EVC, whereas a leaf UNI can only directly communicate with the root UNI in the EVC. Two leaf UNIs cannot communicate with each other directly.

## Slide 85: EVPN Application in a DC
In a cloud DC, the EVPN Network Virtualization Overlay (NVO) solution (RFC8365) can be used.
It is recommended that the data plane use VXLAN encapsulation and the control plane use EVPN to construct a flexible DC overlay network.
VXLAN/EVPN
Spine
Leaf
VAS resource pool
Egress router
Server cluster
All services in the DC are carried over the VXLAN overlay network.
The underlay network consisting of spine and leaf nodes is responsible for high-speed forwarding.

## Slide 86: EVPN Application on a Campus Network
Similar to the cloud DC solution, the campus network virtualization solution can also use EVPN NVO (RFC8365).
On different underlying networks, VXLAN encapsulation is used together with EVPN on the control plane to build a flexible campus overlay network.
Internet/
WAN
AP
LSW
LSW
LSW
LSW
LSW
NGFW
Overlay (virtual network layer)
Virtual network (VN) 1
VN 2
VN 3

## Slide 87: EVPN Application in SD-WAN
SD-WAN is a next-generation enterprise branch interconnection solution that supports features such as intelligent traffic steering, zero touch provisioning (ZTP), and visualization.
In the SD-WAN solution, EVPN can be deployed between the route reflector (RR) and CPE to transmit SD-WAN overlay VPN routes on the control plane. The data plane uses IPsec VPN to build a secure forwarding channel.
Transport network-1
Transport network-2
IPsec VPN
Site1
(CPE)
Site2
(CPE)
1.1.1.1
2.2.2.1
1.1.1.2
2.2.2.2
BGP EVPN route
Site information
Site information
BGP EVPN route
IPsec VPN
RR

## Slide 88
EVPN Background and Terms
EVPN Fundamentals
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations
  Configuring an EVPN to Carry Layer 2 Services
  Configuring an EVPN to Carry Layer 3 Services

## Slide 89: Configuring BD EVPN Functions
An EVPN instance named evpna is created, the EVPN instance view is displayed, and the RD and RT are set to 100:1 and 1:1, respectively.
[Huawei] evpn vpn-instance evpna bd-mode
[Huawei-evpn-instance-evpna] route-distinguisher 100:1
[Huawei-evpn-instance-evpna] vpn-target 1:1 [ both | export-extcommunity | import-extcommunity ]
Configure an EVPN instance in BD mode.
[Huawei] evpn source-address ip-address
Configure an EVPN source address.
The EVPN source address is part of EVPN route information and can be used to identify a PE on an EVPN. Configuring EVPN source addresses is a mandatory task for EVPN configuration.
[Huawei-Eth-Trunk10] esi
Configure an ESI.
Perform this configuration if a VLAN is used to access an EVPN. For details about other configurations, see the product manual of the corresponding product.
Notes: This example describes the configuration commands on Huawei NE20E-S2 (V800R012C10) series routers. For the configuration commands of other models, see the corresponding product manuals.

## Slide 90: Configuring a BD and Binding an EVPN Instance to the BD
[Huawei] bridge-domain 10
[Huawei-bd10] evpn binding vpn-instance evpna [ bd-tag bd-tag ]
Configure an EVPN instance.
In MPLS forwarding, bind a BD to the EVPN instance named evpna. In this example, the BD ID is 10. By specifying different bd-tag values, you can bind multiple BDs with different VLANs to the same EVPN instance and isolate services in these BDs.
[Huawei] interface Eth-Trunk10.1 mode l2
[Huawei-Eth-Trunk10.1] encapsulation dot1q vid 2
[Huawei-Eth-Trunk10.1] rewrite pop single
[Huawei-Eth-Trunk10.1] bridge-domain 10
Add a Layer 2 sub-interface to the BD so that the sub-interface can transmit data packets in this BD.
The Layer 2 sub-interface is added to a BD so that it can transmit data packets in this BD. In this example, the sub-interface ID is Eth-Trunk10.1.
The rewrite pop { single | double } command removes single or double VLAN tags from received packets. For single-tagged packets that a Layer 2 sub-interface receives, specify single to remove the tags from these packets. If the encapsulation type of packets has been set to QinQ in the previous step, specify double to remove double VLAN tags from the received packets.

## Slide 91: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (Dual-Homing Active-Active)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
EVPN needs to be configured on the network to implement Layer 2 communication.
  CE1 is dual-homed to PE1 and PE2 and works in active-active mode through an E-Trunk.
  The ESI of CE1 is 0000.1111.2222.1111.1111.
  IP addresses of CE1 and CE2 are 192.168.1.1/24 and 192.168.1.2/24 respectively.
  The EVPN instance name is evpna.
  On PE1, PE2, and PE3, the RDs of the EVPN instance evpna are 100:1, 200:1, and 300:1 respectively and the RTs are 1:1.
Configuration roadmap
  Configure an IGP on the backbone network to allow the PEs to communicate with each other. (The configuration details are not provided here.)
  Configure basic MPLS functions and enable MPLS LDP to establish LDP LSPs on the backbone network. (The configuration details are not provided here.)
  Configure a BD EVPN instance on PEs.
  Configure an ESI and E-Trunk to implement dual-homing active-active networking.
  Configure local-remote fast reroute (FRR) for MAC routes.
  Establish BGP EVPN peer relationships.
  Configure a CE to access the PEs through an Eth-Trunk interface.
  Verify the configuration.
Notes: The features required in an EVPN dual-homing scenario, such as fast convergence, split horizon, and DF election, all become invalid in a single-homing scenario. In such a scenario, configuring an ESI is optional on a single-homing PE.

## Slide 92: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (1)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
Configure a BD EVPN instance on PEs.
Configure an ESI and E-Trunk to implement dual-homing active-active networking.
Configure local-remote FRR for MAC routes.
Establish BGP EVPN peer relationships.
Configure a CE to access the PEs through the Eth-Trunk interface.
Verify the configuration.
[~PE1] evpn vpn-instance evpna bd-mode
[*PE1-evpn-instance-evpna] route-distinguisher 100:1
[*PE1-evpn-instance-evpna] vpn-target 1:1
[*PE1-evpn-instance-evpna] quit
[*PE1] bridge-domain 10
[*PE1-bd10] evpn binding vpn-instance evpna
[*PE1-bd10] quit
[*PE1] commit
The following uses PE1 as an example to configure an EVPN instance.
The following uses PE1 as an example to configure a source address.
[~PE1] evpn source-address 1.1.1.1
[*PE1] commit

## Slide 93: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (2)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
[~PE1] lacp e-trunk system-id 00e0-fc00-0000
[*PE1] lacp e-trunk priority 1
[*PE1] e-trunk 1
[*PE1-e-trunk-1] peer-address 2.2.2.2 source-address 1.1.1.1
[*PE1-e-trunk-1] quit
[*PE1] interface eth-trunk 10
[*PE1-Eth-Trunk10] mode lacp-static
[*PE1-Eth-Trunk10] e-trunk 1
[*PE1-Eth-Trunk10] e-trunk mode force-master
[*PE1-Eth-Trunk10] esi 0000.1111.2222.1111.1111
[*PE1-Eth-Trunk10] quit
[*PE1] interface eth-trunk 10.1 mode l2
[*PE1-Eth-Trunk10.1] encapsulation dot1q vid 2
[*PE1-Eth-Trunk10.1] rewrite pop single
[*PE1-Eth-Trunk10.1] bridge-domain 10
[*PE1-Eth-Trunk10.1] quit
[*PE1] interface gigabitethernet 0/1/0
[*PE1-GigabitEthernet0/1/0] eth-trunk 10
[*PE1-GigabitEthernet0/1/0] quit
[*PE1] commit
The following uses PE1 as an example to configure an ESI and E-Trunk for dual-homing active-active networking.
The E-Trunk system ID of PE2 must be the same as that of PE1.
Configure a BD EVPN instance on PEs.
Configure an ESI and E-Trunk to implement dual-homing active-active networking.
Configure local-remote FRR for MAC routes.
Establish BGP EVPN peer relationships.
Configure a CE to access the PEs through the Eth-Trunk interface.
Verify the configuration.
Notes: For details about the E-Trunk configuration, see the corresponding product documentation.

## Slide 94: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (3)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
[~PE1] evpn
[*PE1-evpn] vlan-extend private enable
[*PE1-evpn] vlan-extend redirect enable
[*PE1-evpn] local-remote frr enable
[*PE1-evpn] quit
[*PE1] commit
The following uses PE1 as an example to configure local-remote FRR for MAC routes.
In CE multi-homing scenarios, MAC route redirection enables all PEs connected to the same CE to redirect the outbound interfaces of MAC routes destined for the CE to local AC interfaces. This function shortens forwarding paths and improves forwarding efficiency.
If the AC interface on one of the PEs fails, the outbound interface of the associated MAC route can be quickly redirected so that traffic can be forwarded through another active PE, improving reliability.
Configure a BD EVPN instance on PEs.
Configure an ESI and E-Trunk to implement dual-homing active-active networking.
Configure local-remote FRR for MAC routes.
Establish BGP EVPN peer relationships.
Configure a CE to access the PEs through the Eth-Trunk interface.
Verify the configuration.

## Slide 95: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (4)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
[~PE1] bgp 100
[*PE1-bgp] peer 10.0.2.2 as-number 100
[*PE1-bgp] peer 10.0.2.2 connect-interface loopback 1
[*PE1-bgp] peer 10.0.3.3 as-number 100
[*PE1-bgp] peer 10.0.3.3 connect-interface loopback 1
[*PE1-bgp] l2vpn-family evpn
[*PE1-bgp-af-evpn] peer 10.0.2.2 enable
[*PE1-bgp-af-evpn] peer 10.0.3.3 enable
[*PE1-bgp-af-evpn] quit
[*PE1-bgp] quit
[*PE1] commit
The following uses PE1 as an example to establish BGP EVPN peer relationships.
Configure a BD EVPN instance on PEs.
Configure an ESI and E-Trunk to implement dual-homing active-active networking.
Configure local-remote FRR for MAC routes.
Establish BGP EVPN peer relationships.
Configure a CE to access the PEs through the Eth-Trunk interface.
Verify the configuration.

## Slide 96: Example for Configuring Eth-Trunk Sub-interfaces to Access a BD EVPN (5)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
[~CE1] VLAN 2
[*CE1-vlan2] quit
[*CE1] interface Eth-Trunk10
[*CE1-Eth-Trunk10] portswitch
[*CE1-Eth-Trunk10] port link-type trunk
[*CE1-Eth-Trunk10] port trunk allow-pass VLAN 2
[*CE1-Eth-Trunk10] mode lacp-static
[*CE1-Eth-Trunk10] quit
[*CE1] interface gigabitethernet0/1/0
[*CE1-GigabitEthernet0/1/0] eth-trunk 10
[*CE1-GigabitEthernet0/1/0] quit
[*CE1] interface gigabitethernet0/2/0
[*CE1-GigabitEthernet0/2/0] eth-trunk 10
[*CE1-GigabitEthernet0/2/0] quit
[*CE1] commit
The following uses CE1 as an example to configure it to access the PEs through the Eth-Trunk interface.
Configure a BD EVPN instance on PEs.
Configure an ESI and E-Trunk to implement dual-homing active-active networking.
Configure local-remote FRR for MAC routes.
Establish BGP EVPN peer relationships.
Configure a CE to access the PEs through the Eth-Trunk interface.
Verify the configuration.

## Slide 97: Verifying the Configuration (1)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
Check the BGP EVPN peer relationship on PE3.
[~PE3]display bgp evpn peer
BGP local router ID : 10.0.3.3
Local AS number : 100
Total number of peers : 2 Peers in established state : 2
Peer AS State PrefRcv
10.0.1.1 100 Established 4
10.0.2.2 100 Established 4
<PE3>display bgp evpn all routing-table inclusive-route
Local AS number : 100
EVPN address family:
Number of Inclusive Multicast Routes: 3
Route Distinguisher: 100:1
Network(EthTagId/IpAddrLen/OriginalIp) NextHop
*>i 0:32:10.0.1.1 10.0.1.1
Route Distinguisher: 200:1
Network(EthTagId/IpAddrLen/OriginalIp) NextHop
*>i 0:32:10.0.2.2 10.0.2.2
Route Distinguisher: 300:1
Network(EthTagId/IpAddrLen/OriginalIp) NextHop
*> 0:32:10.0.3.3 127.0.0.1
EVPN-Instance evpna:
Number of Inclusive Multicast Routes: 3
Network(EthTagId/IpAddrLen/OriginalIp) NextHop
*>i 0:32:10.0.1.1 10.0.1.1
*>i 0:32:10.0.2.2 10.0.2.2
*> 0:32:10.0.3.3 127.0.0.1
Check Type 3 routes on PE3.
PE3 receives Type 3 routes from PE1 and PE2 to forward BUM traffic.

## Slide 98: Verifying the Configuration (2)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
<PE3>display bgp evpn all routing-table es-route
Local AS number : 100
EVPN address family:
Number of ES Routes: 3
Route Distinguisher: 10.0.1.1:0
Network(ESI) NextHop
*>i 0000.1111.2222.1111.1111 10.0.1.1
Route Distinguisher: 10.0.2.2:0
Network(ESI) NextHop
*>i 0000.1111.2222.1111.1111 10.0.2.2
Route Distinguisher: 10.0.3.3:0
Network(ESI) NextHop
*> 014c.1fcc.f95d.e30a.3100 127.0.0.1
EVPN-Instance evpna:
Number of ES Routes: 1
Network(ESI) NextHop
*> 014c.1fcc.f95d.e30a.3100 127.0.0.1
Check Type 4 routes on PE3.
Type 4 routes sent by PE1 and PE2 carry the same ESI.

## Slide 99: Verifying the Configuration (3)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
<PE3>display bgp evpn all routing-table mac-route
Local AS number : 100
BGP Local router ID is 10.0.3.3
EVPN address family:
Number of Mac Routes: 2
Route Distinguisher: 100:1
Network(EthTagId/MacAddrLen/MacAddr/IpAddrLen/IpAddr) NextHop
*>i 0:48:4c1f-cccf-6675:0:0.0.0.0 10.0.1.1
Route Distinguisher: 300:1
Network(EthTagId/MacAddrLen/MacAddr/IpAddrLen/IpAddr) NextHop
*> 0:48:4c1f-ccf9-5de3:0:0.0.0.0 0.0.0.0
EVPN-Instance evpna:
Number of Mac Routes: 2
Network(EthTagId/MacAddrLen/MacAddr/IpAddrLen/IpAddr) NextHop
*>i 0:48:4c1f-cccf-6675:0:0.0.0.0 10.0.1.1
*> 0:48:4c1f-ccf9-5de3:0:0.0.0.0 0.0.0.0
Check Type 2 routes on PE3.
PE1 sends the MAC address of CE1 to PE3.

## Slide 100: Verifying the Configuration (4)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
<PE3>display bgp evpn all routing-table ad-route
Local AS number : 100
BGP Local router ID is 10.0.3.3
EVPN address family:
Number of A-D Routes: 5
Route Distinguisher: 100:1
Network(ESI/EthTagId) NextHop
*>i 0000.1111.2222.1111.1111:0 10.0.1.1
Route Distinguisher: 200:1
Network(ESI/EthTagId) NextHop
*>i 0000.1111.2222.1111.1111:0 10.0.2.2
EVPN-Instance evpna:
Number of A-D Routes: 4
Network(ESI/EthTagId) NextHop
*>i 0000.1111.2222.1111.1111:0 10.0.1.1
i 10.0.2.2
*> 014c.1fcc.f95d.e30a.3100:0 127.0.0.1
Check Type 1 routes on PE3.
PE1 and PE2 advertise Type 1 routes to implement split horizon.

## Slide 101: Verifying the Configuration (5)
CE1
PE3
CE2
PE2
PE1
GE0/1/0
GE0/2/0
GE0/2/0
Loopback0
10.0.1.1/32
Loopback0
10.0.3.3/32
Loopback0
10.0.2.2/32
VLAN 2
192.168.1.1/24
VLAN 2
192.168.1.2/24
<PE3>display evpn mac routing-table evpn-instance evpna verbose
MAC Flag: D - download to fib
-----------------------------------------------------------------------------EVPN name: evpna
MACs: 2 Entries: 3
MAC Address: 4c1f-cccf-6675
Protocol: BGP VLAN/BD: 10
State: Active Age: 00h13m01s
Type: Dynamic Label: 48002
IndirectID: 0x1000080 PeerIP: 10.0.1.1
Flag: D
TunnelID: 0x0000000001004c4b82 Interface: Ethernet1/0/0
MAC Address: 4c1f-cccf-6675
Protocol: BGP VLAN/BD: 10
State: Active Age: 00h13m01s
Type: Dynamic Label: 48002
IndirectID: 0x100007D PeerIP: 10.0.2.2
Flag: D
TunnelID: 0x0000000001004c4b81 Interface: Ethernet1/0/1
Check the MAC address table of evpna on PE3.
MAC address of CE1
Check the ARP table on CE2 and ping CE1 from CE2.
<CE2>display arp
IP ADDRESS MAC ADDRESS INTERFACE
--------------------------------------------------------------------
192.168.1.2 4c1f-ccf9-5de3 Vlanif2 #MAC address of CE2
192.168.1.1 4c1f-cccf-6675 Eth-Trunk10 #MAC address of CE1
<CE2>ping 192.168.1.1
PING 192.168.1.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.1.1: bytes=56 Sequence=1 ttl=255 time=10 ms
Reply from 192.168.1.1: bytes=56 Sequence=2 ttl=255 time=50 ms
Label allocated by PE1 to CE1

## Slide 102
EVPN Background and Terms
EVPN Fundamentals
Inter-AS EVPN
Typical EVPN Application Scenarios
Basic EVPN Configurations
  Configuring an EVPN to Carry Layer 2 Services
  Configuring an EVPN to Carry Layer 3 Services

## Slide 103: Configuring an EVPN to Carry Layer 3 Services
[Huawei] ip vpn-instance vpna
[Huawei-vpn-instance-vpna] route-distinguisher route-distinguisher
[Huawei-vpn-instance-vpna] vpn-target vpn-target &<1-8> [ both | export-extcommunity | import-extcommunity ] evpn
Configure an L3VPN instance.
Create an L3VPN instance named vpna, enter the L3VPN instance view, and configure an RD and an RT. The keyword evpn needs to be appended to the RT.
[Huawei-vpn-instance-vpna] evpn mpls routing-enable
Enable EVPN to generate and advertise IP prefix routes and IRB routes.
In an EVPN L3VPN scenario, when MPLS or SR-MPLS tunnels are used as public network tunnels, enable EVPN to generate and advertise IP prefix routes and IRB routes so that the local device can advertise IP prefix routes and IRB routes to EVPN peers. If non-MPLS tunnels, such as VXLAN and SRv6 tunnels, are used as public network tunnels, you do not need to run this command.
[Huawei-bgp-vpna] advertise l2vpn evpn
Configure IP prefix route advertisement.
By default, locally leaked routes in a VPN instance are not sent to an EVPN instance. To support mutual access between different VPN instances, enable the function of advertising locally leaked routes from a VPN instance to an EVPN instance so that these routes can be sent to the remote device through a BGP EVPN peer relationship.

## Slide 104: Example for Configuring an EVPN to Carry Layer 3 Services: Requirement Description
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure EVPN on the network to implement Layer 3 communication.
  The gateway address of CE1 is 192.168.1.254/24.
  The gateway address of CE2 is 192.168.2.254/24.
  The L3VPN instance name is vpna.
  On PE1 and PE2, the RDs of the L3VPN instance vpna are 100:1 and 200:1 respectively and the RTs are 1:1.
Configuration roadmap
  Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
  Configure basic MPLS functions and enable MPLS LDP to establish MPLS LSPs on the backbone network. (The configuration details are not provided here.)
  Configure an L3VPN instance on PEs.
  Establish BGP EVPN peer relationships.
  Configure CEs to access PEs and advertise routes.
  Verify the configuration.
P1

## Slide 105: Example for Configuring an EVPN to Carry Layer 3 Services (1)
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
Configure basic MPLS functions and enable MPLS LDP to establish MPLS LSPs on the backbone network.
Configure an L3VPN instance on PEs.
Establish BGP EVPN peer relationships.
Configure CEs to access PEs and advertise routes.
Verify the configuration.
P1
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 1:1 both evpn
[*PE1-vpn-instance-vpna-af-ipv4] evpn mpls routing-enable
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1] commit
The following uses PE1 as an example to configure an L3VPN instance.
[~PE1] bgp 100
[*PE1-bgp] peer 10.0.3.3 as-number 100
[*PE1-bgp] peer 10.0.3.3 connect-interface loopback 0
[*PE1-bgp] l2vpn-family evpn
[*PE1-bgp-af-evpn] peer 10.0.3.3 enable
[*PE1-bgp-af-evpn] quit
[*PE1-bgp] quit
[*PE1] commit
The following uses PE1 as an example to establish BGP EVPN peer relationships.

## Slide 106: Example for Configuring an EVPN to Carry Layer 3 Services (2)
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
Configure basic MPLS functions and enable MPLS LDP to establish MPLS LSPs on the backbone network.
Configure an L3VPN instance on PEs.
Establish BGP EVPN peer relationships.
Configure CEs to access PEs and advertise routes.
Verify the configuration.
P1
[~PE1] interface GigabitEthernet 0/1/0
[*PE1-GigabitEthernet0/1/0] ip binding vpn-instance vpna
[*PE1-GigabitEthernet0/1/0] ip address 192.168.1.254 255.255.255.0
[*PE1-GigabitEthernet0/1/0] quit
[*PE1] commit
The following uses PE1 as an example to configure CEs to access PEs.
[~PE1] bgp 100
[~PE1-bgp] ipv4-family vpn-instance vpna
[~PE1-bgp-vpna] import-route direct
[~PE1-bgp-vpna] advertise l2vpn evpn
[~PE1-bgp-vpna] quit
[~PE1-bgp] quit
[~PE1] commit
The following uses PE1 as an example to configure CE-side route advertisement.

## Slide 107: Verifying the Configuration (1)
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
Configure basic MPLS functions and enable MPLS LDP to establish MPLS LSPs on the backbone network.
Configure an L3VPN instance on PEs.
Establish BGP EVPN peer relationships.
Configure CEs to access PEs and advertise routes.
Verify the configuration.
P1
<PE1>display bgp evpn all routing-table prefix-route
Local AS number : 100
BGP Local router ID is 10.0.1.1
EVPN address family:
Number of Ip Prefix Routes: 2
Route Distinguisher: 100:1
Network(EthTagId/IpPrefix/IpPrefixLen) NextHop
*> 0:192.168.1.0:24 0.0.0.0
Route Distinguisher: 200:1
Network(EthTagId/IpPrefix/IpPrefixLen) NextHop
*>i 0:192.168.2.0:24 10.0.3.3
Check Type 5 routes on PE1.
This is the Type 5 route advertised by PE3.

## Slide 108: Verifying the Configuration (2)
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
Configure basic MPLS functions and enable MPLS LDP to establish MPLS LSPs on the backbone network.
Configure an L3VPN instance on PEs.
Establish BGP EVPN peer relationships.
Configure CEs to access PEs and advertise routes.
Verify the configuration.
P1
[~PE1]display bgp evpn all routing-table prefix-route 0:192.168.2.0:24
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(200:1): 1
BGP routing table entry information of 0:192.168.2.0:24:
Label information (Received/Applied): 48005/NULL
From: 10.0.3.3 (10.0.13.3)
Route Duration: 0d01h29m51s
Relay IP Nexthop: 10.0.13.3
Relay Tunnel Out-Interface: LDP LSP #The outer tunnel is an LDP tunnel.
Original nexthop: 10.0.3.3
Qos information : 0x0
Ext-Community: RT <1 : 1>
AS-path Nil, origin incomplete, MED 0, localpref 100, pref-val 0, valid, intern
al, best, select, pre 255, IGP cost 1
Route Type: 5 (Ip Prefix Route)
Ethernet Tag ID: 0, IP Prefix/Len: 192.168.2.0/24, ESI: 0000.0000.0000.0000.000
0, GW IP Address: 0.0.0.0
Not advertised to any peer yet
Check detailed information about Type 5 routes on PE1.
This label is allocated by PE3.

## Slide 109: Verifying the Configuration (3)
CE1
CE2
GE0/1/0
GE0/2/0
PE1
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
PE2
Loopback0
10.0.3.3/32
192.168.1.1/24
192.168.2.1/24
Configure an IGP on the backbone network to allow the PEs to communicate. (The configuration details are not provided here.)
Configure basic MPLS functions and enable MPLS LDP to establish LDP LSPs on the backbone network.
Configure an L3VPN instance on PEs.
Establish BGP EVPN peer relationships.
Configure CEs to access PEs and advertise routes.
Verify the configuration.
P1
<PE1>display ip routing-table vpn-instance vpna
------------------------------------------------
Routing Table : vpna
Destination/Mask Proto NextHop Interface
192.168.1.0/24 Direct 192.168.1.254 GigabitEthernet0/1/0 192.168.2.0/24 IBGP 10.0.3.3 GigabitEthernet0/2/0
Check the routing table of vpna on PE1.
<CE1>ping 192.168.2.1
PING 192.168.2.1: 56 data bytes, press CTRL_C to break
Reply from 192.168.2.1: bytes=56 Sequence=1 ttl=126 time=30 ms
Reply from 192.168.2.1: bytes=56 Sequence=2 ttl=126 time=10 ms
Reply from 192.168.2.1: bytes=56 Sequence=3 ttl=126 time=50 ms
Reply from 192.168.2.1: bytes=56 Sequence=4 ttl=126 time=40 ms
Reply from 192.168.2.1: bytes=56 Sequence=5 ttl=126 time=50 ms
--- 192.168.2.1 ping statistics ---
5 packet(s) transmitted
5 packet(s) received
0.00% packet loss
round-trip min/avg/max = 10/36/50 ms
Ping 192.168.2.1 from CE1.

## Slide 110
(Single-answer question) Which of the following route types is used by EVPN to implement fast convergence? ( )
  Type 1
  Type 2
  Type 3
  Type 4
(Single-answer question) Which of the following types of routes carries the MPLS label used for forwarding unicast data? ( )
  Type 1
  Type 2
  Type 3
  Type 4
Notes: A
B

## Slide 111
EVPN uses BGP extensions to implement MAC address learning and advertisement on the control plane instead of the data plane. EVPN allows a device to manage MAC addresses in the same way as it manages routes, implementing load balancing between EVPN routes with the same destination MAC address but different next hops. In addition, EVPN supports the deployment of BGP RRs, significantly reducing network complexity.
EVPN uses the labels carried in Type 3 routes to guide BUM traffic forwarding, uses the labels carried in Type 2 routes to guide unicast traffic forwarding, uses Type 1 routes to implement split horizon and fast convergence, and uses Type 4 routes to implement DF election and automatic ES member discovery. EVPN also supports the advertisement of IP prefix routes through Type 5 routes.
With the enrichment of application scenarios and extension of protocols, EVPN can be used in various scenarios, including WAN, DC, and campus network scenarios.