## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2020.07.15
Li Xianzhi/00354681
New
Lu Yueyue/WX445705
2021.10.15
He Junjian/WX580230
Update

## Slide 2: IPv6 Routing

## Slide 3
With the advent of the Internet of Everything (IoE), IPv4 address space is running out. It is imperative that we replace IPv4 with IPv6. How do we enable reachability between nodes on an IPv6 network? Similar to an IPv4 network, an IPv6 network also supports static routes and dynamic routing protocols.
IPv6 static routes and IPv4 static routes are configured in a similar way. To support IPv6 networks, the Internet Engineering Task Force (IETF) defines Open Shortest Path First version 3 (OSPFv3) and extends Intermediate System to Intermediate System (IS-IS) and Border Gateway Protocol (BGP).
This course describes the concepts and configurations of IPv6 static routes and common IPv6 dynamic routing protocols, including OSPFv3, IS-IS (IPv6), and BGP4+.

## Slide 4
On completion of this course, you will be able to:
  Configure IPv6 static routes.
  Analyze the differences between OSPFv3 and OSPFv2.
  Configure basic OSPFv3 functions.
  Describe the IS-IS extensions for IPv6.
  Configure basic IS-IS (IPv6) functions.
  Describe the BGP extensions for IPv6.
  Configure basic BGP4+ functions.

## Slide 5
IPv6 Static Routes
OSPFv3 Implementation and Configurations
IS-IS (IPv6) Implementation and Configurations
BGP4+ Implementation and Configurations

## Slide 6: IPv6 Static Routes
Similar to IPv4 static routes, IPv6 static routes are configured by the administrator and are applicable to IPv6 networks with simple structures.
When creating an IPv6 static route, you can specify both the outbound interface and next hop, or specify only the outbound interface or next hop.
  Point-to-point (P2P) interface: specify the outbound interface.
  Broadcast interface: specify the next hop.
Load balancing and backup:
  Setting the same preference value for IPv6 static routes to the same destination implements load balancing among these routes, whereas setting different preference values for such routes implements route backup.
Notes: IPv6 static routes and IPv4 static routes differ mainly in destination and next-hop IP addresses. IPv6 static routes use IPv6 addresses, whereas IPv4 static routes use IPv4 addresses.

## Slide 7: Basic Commands for Configuring IPv6 Static Routes
Precautions:
  If no preference is set for a static route, the static route uses the default preference 60.
  If both the destination address and prefix length are set to all zeros (:: 0), the default route (::/0) is configured.
  If permanent is specified in a command of the undo form, permanent advertisement is disabled for the IPv6 static route, but this route is not deleted.
Configure an IPv6 static route on the public network:
Configure an IPv6 static route in a VPN instance:
[Huawei] ipv6 route-static dest-ipv6-address prefix-length { interface-type interface-number [ nexthop-ipv6-address ] | nexthop-ipv6-address | vpn-instance vpn-destination-name nexthop-ipv6-address } [ preference preference][ permanent | inherit-cost ] [ description text ]
[Huawei] ipv6 route-static vpn-instance vpn-instance-name dest-ipv6-address prefix-length { [ interface-type interface-number [ nexthop-ipv6-address ] ] | nexthop-ipv6-address [ public ] | vpn-instance vpn-destination-name nexthop-ipv6-address } [ preference preference ] [permanent | inherit-cost ] [ description text ]
Notes: [Huawei] ipv6 route-static dest-ipv6-address prefix-length { interface-type interface-number [ nexthop-ipv6-address ] | nexthop-ipv6-address | vpn-instance vpn-destination-name nexthop-ipv6-address } [ preference preference][ permanent | inherit-cost ] [ description text ]
  preference preference: specifies a preference value for the route. The value is an integer ranging from 1 to 255. The default value is 60.
  permanent: enables the function of permanently advertising the IPv6 static route.
  inherit-cost: enables the static route to inherit the cost of the recursive route.
  description text: specifies a description for the static route. The value is a string of 1 to 80 characters and can contain spaces.
[Huawei] ipv6 route-static vpn-instance vpn-instance-name dest-ipv6-address prefix-length { [ interface-type interface-number [ nexthop-ipv6-address ] ] | nexthop-ipv6-address [ public ] | vpn-instance vpn-destination-name nexthop-ipv6-address } [ preference preference ] [ permanent | inherit-cost ] [ description text ]
  public: indicates that nexthop-ipv6-address is a public network address instead of an address in the source VPN instance.

## Slide 8: Example for Configuring IPv6 Static Routes
R1
R2
GE0/0/1
GE0/0/1
Device | Interface | IPv6 Address
R1 | GE0/0/1 | 2001:DB8:2345:12::1/64
 | Loopback0 | 2001:DB8:2345:1::1/128
R2 | GE0/0/1 | 2001:DB8:2345:12::2/64
 | Loopback0 | 2001:DB8:2345:2::2/128
Scenario description:
  A company has an IPv6 network deployed for service testing. In the initial deployment phase, static routes are used to implement interconnection and communication over the IPv6 network.
  Specifically, static routes are used to enable communication between loopback0 interfaces of R1 and R2.
1. Assign an IPv6 address to each router interface. (The configuration details are not provided here.)
2. Configure IPv6 static routes.
3. Test the IPv6 network connectivity.
[R1] ipv6 route-static 2001:DB8:2345:2::2 128 2001:DB8:2345:12::2
[R2] ipv6 route-static 2001:DB8:2345:1::1 128 2001:DB8:2345:12::1
[R1] ping ipv6 2001:DB8:2345:2::2
PING 2001:DB8:2345:2::2 : 56 data bytes, press CTRL_C to break
Reply from 2001:DB8:2345:2::2
bytes=56 Sequence=1 hop limit=64 time = 90 ms
Reply from 2001:DB8:2345:2::2
bytes=56 Sequence=2 hop limit=64 time = 20 ms
Reply from 2001:DB8:2345:2::2
bytes=56 Sequence=3 hop limit=64 time = 20 ms
Reply from 2001:DB8:2345:2::2
bytes=56 Sequence=4 hop limit=64 time = 20 ms
Reply from 2001:DB8:2345:2::2
bytes=56 Sequence=5 hop limit=64 time = 20 ms
--- 2001:DB8:2345:2::2 ping statistics ---
5 packet(s) transmitted
5 packet(s) received
0.00% packet loss
round-trip min/avg/max = 20/34/90 ms

## Slide 9
IPv6 Static Routes
OSPFv3 Implementation and Configurations
  OSPFv3 Implementation
  Basic OSPFv3 Configurations
IS-IS (IPv6) Implementation and Configurations
BGP4+ Implementation and Configurations

## Slide 10: OSPFv3 Overview
OSPF is a link-state Interior Gateway Protocol (IGP) defined by the IETF. Currently, OSPF version 2 (OSPFv2) is intended for IPv4, and OSPF version 3 (OSPFv3) is intended for IPv6.
OSPFv3 is mainly developed as a routing protocol independent of any specific network layer. The internal routing information of OSPFv3 has been redesigned to serve this purpose.
OSPFv2 is an IGP running over IPv4, whereas OSPFv3 is an IGP running over IPv6. They are not compatible.
Overview
Implementation
Packets
LSAs
Data link layer
IPv4
IPv6
OSPFv2
OSPFv3

## Slide 11: Similarities Between OSPFv3 and OSPFv2
OSPF's basic running mechanisms remain unchanged, including:
  Basic concepts:
    Area division and router types
    Parameters that affect route calculation: preference and cost
    Supported network types: broadcast, non-broadcast multiple access (NBMA), P2P, and point-to-multipoint (P2MP)
    Packet types: Hello, database description (DD), link state request (LSR), link state update (LSU), and link state acknowledgment (LSAck)
  Working mechanisms:
    Establishment of neighbor relationships and transition of the neighbor relationship status
    Election of the Designated router (DR) and backup DR (BDR)
    Link state advertisement (LSA) flooding
    Route calculation process
Overview
Implementation
Packets
LSAs
Notes: Similarities also include support for special areas, support for virtual links, and multi-process support.
For details, see the "HCIP-Datacom-Core Technology" course.

## Slide 12: OSPFv3 Topology and Router Types
Area 0
Area 1
Area 2
Area 3
ASBR
ABR
ABR
ABR
Metro network core
District-county aggregation
District-county aggregation
District-county aggregation
IR
IR
IR
IR
IR
IR
IR
IR
IR
BGP
Import of external routes
Internal router (IR)
Area border router (ABR)
Autonomous system boundary router (ASBR)
BR
BR
BR
BR
Backbone router (BR)
Overview
Implementation
Packets
LSAs

## Slide 13: OSPFv3 and OSPFv2 Have Similar Working Mechanisms
R1
R2
R3
LSA
LSA
LSA
R1
R2
R3
Neighbor relationship establishment
Neighbor relationship establishment
Neighbor relationship establishment
R1
R2
R3
R1
R2
R3
Path computation
1
2
3
LSDB
LSDB
LSDB
Routing table
Routing entry generation
1
2
3
4
Path computation
Path computation
Routing table
Routing table
Overview
Implementation
Packets
LSAs

## Slide 14: Differences Between OSPFv3 and OSPFv2
OSPFv3 runs and performs topology calculation based on links instead of network segments.
OSPFv3 supports multiple instances per link.
OSPFv3 packets and LSAs do not contain IP addresses, and the packet and LSA formats are reconstructed.
  OSPFv3 packets and router-LSAs/network-LSAs do not contain IP addresses.
  OSPFv3 LSAs define the flooding scopes of LSAs.
  OSPFv3 has new types of LSAs defined to carry IPv6 addresses and prefixes.
  OSPFv3 neighbors are identified only by router IDs, not by IP addresses.
Overview
Implementation
Packets
LSAs

## Slide 15: Unique Neighbor ID: Router ID
OSPFv3 uses router IDs to identify network devices.
2001:DB8:2345:1::1/64
2001:DB8:2345:2::1/64
2001:DB8:2345:3::1/64
2001:DB8:2345:4::1/64
OSPFv3
Router ID: 10.1.1.1
Router ID: 10.1.2.2
Router ID: 10.1.3.3
Router ID: 10.1.4.4
A router ID uniquely identifies an OSPFv3 device in an AS. If no router ID is configured, an OSPFv3 process cannot run.
When you configure a router ID for a device, ensure that the router ID in an AS is unique.
A router ID is a 32-bit local identifier, which is not related to IPv6 addresses and is expressed in dotted decimal notation.
Overview
Implementation
Packets
LSAs
Notes: On broadcast, NBMA, P2P, and P2MP networks, OSPFv2 uses IPv4 interface addresses to identify neighbors. On virtual-link networks, however, OSPFv2 uses router IDs to identify neighbors.

## Slide 16: OSPFv3 Operation Based on Links
OSPFv3 operates based on links. Devices can establish a neighbor relationship as long as they are on the same link.
OSPFv2 operation based on network segments
OSPFv3 operation based on links
OSPFv3 runs between R1 and R2.
GE0/0/1 of R1 and that of R2 reside on different network segments, but R1 and R2 can still establish an OSPFv3 neighbor relationship.
When OSPFv3 is running, two neighbors only need to be on the same direct link.
OSPFv3
R1
R2
OSPFv2
R1
R2
OSPFv2 runs between R1 and R2.
The OSPFv2 neighbor relationship can be established between R1 and R2 only when the IP addresses of GE0/0/1 on R1 and that on R2 belong to the same network segment.
When OSPFv2 is running, two neighbors must be on the same network segment.
GE0/0/1
10.1.12.1/24
GE0/0/1
10.1.12.2/24
GE0/0/1
2001:DB8:2345:1::1/64
GE0/0/1
2001:DB8:2345:2::1/64
Overview
Implementation
Packets
LSAs
Notes: IPv6 emphasizes the link concept. Multiple IPv6 prefixes that indicate different IP subnets can be allocated to the same link. Different from IPv4, IPv6 allows two nodes on the same link to communicate even if they do not have the same IPv6 prefix. This greatly changes the OSPF behavior.
In OSPFv3, the concepts "link" and "prefix" are frequently used, which however are independent of each other. The terms "network" and "subnet" used in OSPFv2 should be replaced with the term "link" when OSPFv3 is discussed.

## Slide 17: Multi-Instance Support by Links
An OSPFv3 physical interface can be bound to multiple instances, which are identified by different instance IDs. A single physical link can run multiple OSPFv3 instances.
These OSPFv3 instances can each establish a neighbor relationship with the device at the remote end of the link, send packets to the remote device, and do not interfere with each other, thereby fully sharing resources on the same link.
By using instance IDs, R2 and R3 can establish an OSPFv3 neighbor relationship, and R1 and R4 can also establish an OSPFv3 neighbor relationship.
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/1
GE0/0/1
Instance 1
Instance 2
Overview
Implementation
Packets
LSAs
Notes: In multi-instance, each instance is differentiated by adding a specific instance ID to the OSPFv3 packet header. If an instance is assigned a specific instance ID, the OSPFv3 packets that do not match the instance ID are discarded.

## Slide 18: Use of Link-local Addresses by OSPFv3
OSPFv3 uses the link-local address (FE80::/10) as the source address of packets to be sent and the next-hop address of OSPFv3 routes.
  Link-local addresses are used to maintain neighbor relationships and synchronize link state databases (LSDBs).
Advantages:
  OSPFv3 can calculate topologies without global IPv6 unicast addresses, separating topologies from addresses.
  OSPFv3 packets are not forwarded beyond the originating link, reducing unnecessary packet flooding and saving bandwidth.
GE0/0/1
2001:DB8:2345:12::2/64
OSPFv3
R1
R2
2001:DB8:2345:2::2/128
Loopback0
[R1]display ipv6 routing-table
……
Destination: 2001:DB8:2345:2::2 PrefixLength : 128
NextHop: FE80::2E0:FCFF:FE82:522B Preference : 10
Cost: 1 Protocol : OSPFv3
RelayNextHop: :: TunnelID : 0x0
Interface: GigabitEthernet0/0/1 Flags : D
……
GE0/0/1
2001:DB8:2345:12::1/64
Overview
Implementation
Packets
LSAs
Notes: IPv6 implements neighbor discovery and automatic configuration using link-local addresses. Routers running IPv6 do not forward IPv6 packets whose destination addresses are link-local addresses. Such packets are valid only on the local link.
OSPFv3 is a routing protocol running on IPv6 and uses link-local addresses to send OSPFv3 packets.
  OSPFv3 assumes that each router has been assigned a link-local address on each link. All OSPFv3 interfaces except virtual-link interfaces use the associated link-local addresses as the source addresses to send OSPFv3 packets.
  A router learns the link-local addresses of all the other routers attached to the same link and uses these addresses as the next-hop addresses to forward packets.
  Note: Description of link-local addresses is only contained in link-LSAs (new type of LSA supported in OSPFv3).
Note: On a virtual link, the global unicast address or a site's local address must be used as the source address of OSPFv3 packets.

## Slide 19: OSPFv3 Packets
OSPFv3 and OSPFv2 have the same types of packets:
  Hello, DD, LSR, LSU, and LSAck packets
OSPFv3 and OSPFv2 use the same protocol number 89.
  OSPFv2: The Protocol in the IPv4 packet header is 89.
  OSPFv3: The Next Header in the IPv6 packet header is 89.
Similar to OSPFv2, OSPFv3 uses a multicast address as the destination address of OSPF packets.
  OSPFv2 uses IPv4 multicast addresses:
    OSPF IGP routers use 224.0.0.5, whereas the OSPF IGP DR uses 224.0.0.6.
  OSPFv3 uses IPv6 multicast addresses:
    OSPF IGP routers use FF02::5, whereas the OSPF IGP DR uses FF02::6.
Overview
Implementation
Packets
LSAs
Notes: OSPFv3 packets have the following functions:
  Hello packet: Hello packets are sent periodically to discover, establish, and maintain OSPFv3 neighbor relationships.
  DD packet: A DD packet describes the summary of a local LSDB and is used for LSDB synchronization between two devices.
  LSR packet: An LSR packet is used to request the required LSAs from a neighbor. An OSPFv3 device sends LSR packets to its neighbor only after DD packets have been successfully exchanged between them.
  LSU packet: An LSU packet is sent to a neighbor to provide required LSAs.
  LSAck packet: An LSAck packet is used to acknowledge the received LSAs.

## Slide 20: OSPFv3 Packet Header
OSPFv2 packet header:
OSPFv3 packet header:
Similar to OSPFv2, OSPFv3 defines the same packet header for its five types of packets. However, some fields in the OSPFv3 packet header differ from those in the OSPFv2 packet header.
Changes:
  Instance ID: 1 byte. The default value is 0. This field allows multiple OSPFv3 instances to be run on a link. Each instance has a unique instance ID. The instance ID is valid only on the local link.
  All authentication fields are removed from the OSPFv3 packet header: OSPFv3 authentication can be implemented using IPv6's authentication and security processing mechanism. In addition, OSPFv3 packets can be authenticated using OSPFv3's own mechanism.
Version=3 | Type | Packet Length | 
Router ID |  |  | 
Area ID |  |  | 
Checksum |  | Instance ID | 0
Version=2 | Type | Packet Length
Router ID |  | 
Area ID |  | 
Checksum |  | Auth Type
Authentication |  | 
Overview
Implementation
Packets
LSAs
Notes: Version: indicates the OSPF version, and occupies 1 byte. For OSPFv3, the value is 3.
Type: indicates the type of an OSPFv3 packet and occupies 1 byte. The following types are available:
  1: Hello packet
  2: DD packet
  3: LSR packet
  4: LSU packet
  5: LSAck packet
Packet length: indicates the total length of an OSPFv3 packet, including the packet header. The field occupies 2 bytes.
Router ID: indicates the router ID of the router that originates the packet, and occupies 4 bytes.
Area ID: indicates the area in which the packet is sent, and occupies 4 bytes.
Checksum: indicates the standard 16-bit IPv6 checksum and occupies 2 bytes.
0: Occupying 1 byte, this field is reserved and must be set to 0.

## Slide 21: Hello Packet
OSPFv2 Hello packet format
OSPFv3 Hello packet format
Compared with OSPFv2 Hello packets, OSPFv3 Hello packets do not contain the Network Mask field but newly contain the Interface ID field, which identifies the interface that sends the Hello packets.
Changes:
  Interface ID: uniquely identifies the interface that sends Hello packets to establish a connection, and occupies 4 bytes.
  Options: indicates the optional capabilities supported by a device. This field is extended to 3 bytes. Compared with OSPFv2, OSPFv3 adds the R bit and the V6 bit.
    AT: indicates whether OSPFv3 authentication is supported.
    R: indicates whether the originating router has the forwarding capability.
    V6: If the V6 bit is set to 0, the router or link does not participate in IPv6 route calculation.
Network Mask |  | 
HelloInterval | Options | Rtr Pri
RouterDeadInterval |  | 
Designated Router |  | 
Backup Designated Router |  | 
Neighbor |  | 
Interface ID |  | 
Rtr Pri | Options | 
HelloInterval |  | RouterDeadInterval
Designated Router ID |  | 
Backup Designated Router ID |  | 
Neighbor ID |  | 
0 | AT | / | / | / | / | DC | R | NP | MC | E | V6
0
18
24
13
Overview
Implementation
Packets
LSAs
Notes: Rot Pri: indicates the router's router priority, which is used for DR election. This field occupies 1 byte, and the default value is 1. If it is set to 0, the router cannot participate in DR or BDR election.
Options: indicates the optional capabilities supported by the router and occupies 3 bytes.
  AT: indicates whether OSPFv3 authentication is supported. This option occupies 1 bit. If the AT bit is 1, an authentication tail field containing authentication information is added to the OSPFv3 packet.
  DC: indicates whether the capability of processing demand circuits is supported. This option occupies 1 bit.
  R: indicates whether the originator is a valid router. This option occupies 1 bit.
  NP: indicates whether the area to which the originating router interface belongs is a not-so-stubby area (NSSA). This option occupies 1 bit.
  MC: indicates whether multicast data packets can be forwarded. This option occupies 1 bit.
  E: indicates whether external routes are supported. This option occupies 1 bit.
  V6: indicates whether the router or link can participate in route calculation. This option occupies 1 bit. If it is set to 0, the router or link does not participate in IPv6 route calculation.

## Slide 22
Notes: HelloInterval: indicates the interval at which Hello packets are sent. This field occupies 2 bytes.
RouterDeadInterval: indicates a Dead interval. This field occupies 2 bytes. If a device does not receive any Hello packets from its neighbors within a specified Dead interval, the neighbors are considered to be down.
Designated Router ID: indicates the router ID of the DR. This field occupies 4 bytes.
Backup Designated Router ID: indicates the router ID of the BDR. This field occupies 4 bytes.
Neighbor ID: indicates the router ID of a neighbor. This field occupies 4 bytes.
Note: The formats of DD, LSR, LSU, and LSAck packets are similar to those of OSPFv2, and therefore are not provided in this course.

## Slide 23: OSPFv3 LSA Header
OSPFv2
OSPFv3
Compared with the OSPFv2 LSA header, the OSPFv3 LSA header does not contain the Options field but has the LS Type field expanded. OSPFv3 also uses the LS Type, Link State ID, and Advertising Router fields to uniquely identify an LSA.
Changes:
  LS Type: indicates the link state type. This field is extended to 2 bytes.
    U: indicates how to process unknown LSAs. This field occupies 1 bit.
    S2/S1: indicates the LSA flooding scope. This field occupies 2 bits.
    LSA Function Code: identifies the LSA type. This field occupies 13 bits.
LS Age | Options | LS Type
Link State ID |  | 
Advertising Router |  | 
LS Sequence Number |  | 
LS Checksum | Length | 
U | S2 | S1 | LSA Function Code
LS Age | LS Type
Link State ID | 
Advertising Router | 
LS Sequence Number | 
LS Checksum | Length
Overview
Implementation
Packets
LSAs
Notes: LS Age: indicates the time elapsed since the LSA was generated, in seconds. This field occupies 2 bytes. The value of this field continually increases regardless of whether the LSA is transmitted over a link or saved in an LSDB.
LS Type: indicates the LSA type. This field occupies 2 bytes. The high-order three bits of this field identify generic properties of the LSA, whereas the remaining bits identify the LSA's specific function.
  The U-bit indicates how to process an unknown LSA, that is, how a router that does not recognize an LSA's function code should process this LSA.
    0: The LSA is treated as if it had the link-local flooding scope.
    1: The LSA is stored and flooded as if its type had been understood.
  The S2 and S1 bits indicate the flooding scope of the LSA.
    S2 S1 = 0 0: link-local flooding scope. The LSA is flooded only on the originating link.
    S2 S1 = 0 1: area flooding scope. The LSA is flooded to all routers in the originating area.
    S2 S1 = 1 0: AS flooding scope. The LSA is flooded to all routers in the local AS.
    S2 S1 = 1 1: reserved.

## Slide 24
Notes: Link State ID: indicates a local 32-bit identifier, which is irrelevant to an IPv6 address, and occupies 4 bytes. This field, together with the LS Type and Advertising Router fields, describes an LSA in the OSPFv3 domain. Compared with OSPFv2, OSPFv3 does not contain address information in the Link State ID field.
Advertising Router: indicates the router ID of the router that generates the LSA. This field occupies 4 bytes.
LS Sequence Number: indicates the sequence number of the LSA. This field occupies 4 bytes. Neighbors can use this field to identify the latest LSA.
LS Checksum: checksum of all fields except the LS Age field. The LS Checksum field occupies 2 bytes.
Length: indicates the total length of the LSA, including the LSA header. This field occupies 2 bytes.

## Slide 25: OSPFv3 LSA Types
Compared with OSPFv2, OSPFv3 LSAs have similar names but slightly different functions.
OSPFv3 supports two new types of LSAs: link-LSA and intra-area-prefix-LSA.
OSPFv2 LSAs |  | OSPFv3 LSAs |  | Similarities and Differences
Type | Name | Type | Name | 
1 | Router-LSA | 0x2001 | Router-LSA | The functions are similar, but the OSPFv3 LSAs no longer describe address information. Instead, they only describe topology structures.
2 | Network-LSA | 0x2002 | Network-LSA | 
3 | Network-summary-LSA | 0x2003 | Inter-area-prefix-LSA | The functions are similar, but the names are different.
4 | ASBR-summary-LSA | 0x2004 | Inter-area-router-LSA | 
5 | AS-external-LSA | 0x4005 | AS-external-LSA | The functions and names are the same.
7 | NSSA-LSA | 0x2007 | NSSA-LSA | 
 |  | 0x0008 | Link-LSA | New in OSPFv3
 |  | 0x2009 | Intra-area-prefix-LSA | 
Overview
Implementation
Packets
LSAs
Notes: As shown in the figure, the U-bit in the LS Type field of the OSPFv3 LSA header is 0 by default. Except the Type 5 and Type 8 LSAs, the other types of LSAs all have the area flooding scope (S2 S1 = 0 1).
  Link-local flooding scope: LSAs, including link-LSAs, are flooded only on the local link.
  Area flooding scope: The following types of LSAs are flooded in a single OSPF area: router-LSA, network-LSA, inter-area-prefix-LSA, inter-area-router-LSA, NSSA-LSA, and intra-area-prefix-LSA.
  AS flooding scope: LSAs, including AS-external-LSAs, are flooded in an entire routing domain (AS).

## Slide 26: Type 1: Router-LSA
OSPFv2
OSPFv3
In OSPFv2, the Link Type, Link ID, and Link Data fields are used to describe an interface. In OSPFv3, a device generates an LSA for each area where OSPFv3 interfaces reside. The LSA describes the link state information (Link Type, Interface ID, Neighbor Interface ID, and Neighbor Router ID) and link cost of the device and is flooded in the area where the device resides.
Description of key fields:
  Link Type: indicates the link type and occupies 1 byte.
  Interface ID: indicates the interface ID and occupies 4 bytes.
  Neighbor Interface ID: indicates the interface ID of a neighbor and occupies 4 bytes.
  Neighbor Router ID: indicates the router ID of a neighbor and occupies 4 bytes.
0 | V | E | B | 0 | # Links
Link ID |  |  |  |  | 
Link Data |  |  |  |  | 
Link Type |  |  |  | # Tos | Metric
0 | W | V | E | B | Options | 
Link Type |  |  |  | 0 |  | Metric
Interface ID |  |  |  |  |  | 
Neighbor Interface ID |  |  |  |  |  | 
Neighbor Router ID |  |  |  |  |  | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 router-LSA are described as follows:
  W: wildcard receiver. The value 1 indicates that the router supports multicast routes.
  V: virtual link. The value 1 indicates that the router that generates the LSA is at one end of the virtual link.
  E: external. The value 1 indicates that the router that generates the LSA is an ASBR.
  B: border. The value 1 indicates that the router that generates the LSA is an ABR.
  Options: indicates the optional capabilities supported by the router and occupies 3 bytes.
    DC: indicates whether the capability of processing demand circuits is supported. This option occupies 1 bit.
    R: indicates whether the originator is a valid router. This option occupies 1 bit.
    NP: indicates whether the area to which the originating router interface belongs is a not-so-stubby area (NSSA). This option occupies 1 bit.

## Slide 27
Notes:     MC: indicates whether multicast data packets can be forwarded. This option occupies 1 bit.
    E: indicates whether external routes are supported. This option occupies 1 bit.
    V6: indicates whether the router or link can participate in route calculation. This option occupies 1 bit. If it is set to 0, the router or link does not participate in IPv6 route calculation.
  Link Type: indicates the link type and occupies 1 byte.
    1: The router is connected to another router in P2P mode.
    2: The router is connected to a transit network.
    3: reserved.
    4: virtual link.
  Metric: indicates the cost of the traffic outbound interface and occupies 2 bytes.

## Slide 28: Type 2: Network-LSA
OSPFv2
OSPFv3
Compared with OSPFv2, OSPFv3 network-LSAs do not contain the Network Mask field. Instead, OSPFv3 network-LSAs describe the link state of the local network segment only by using the router IDs of the attached routers. Network-LSAs are generated by the DR and flooded in the area to which the DR belongs.
Description of key fields:
  Attached Router: indicates the router ID of each router connected to the same network segment, including the router ID of the DR, and occupies 4 bytes.
Network Mask
Attached Router
Attached Router
……
0 | Options
Attached Router | 
Attached Router | 
…… | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 network-LSA are described as follows:
  Options: same as the Options field in a router-LSA.

## Slide 29: Type 3: Inter-Area-Prefix-LSA
OSPFv2: network-summary-LSA
OSPFv3
PrefixOptions:
Similar to a network-summary-LSA in OSPFv2, an inter-area-prefix-LSA in OSPFv3 is generated by an ABR to describe routes with an IPv6 address prefix in an area and is advertised to the other related areas. An ABR sends a Type 3 LSA for each IPv6 address prefix.
Description of key fields (triplet of a prefix):
  PrefixLength: indicates the number of bits in the prefix and occupies 1 byte.
  PrefixOptions: describes some capabilities associated with the prefix so that specific judgment and processing can be performed during various routing calculations. This field occupies 1 byte. Format of the PrefixOptions field:
    P-bit: indicates the propagate bit and occupies 1 bit.
    MC-bit: indicates the multicast bit and occupies 1 bit.
    LA-bit: indicates the "local address" capability bit and occupies 1 bit.
    NU-bit: indicates the "no unicast" capability bit and occupies 1 bit.
  Address Prefix: indicates the IPv6 address prefix with a variable length.
Network Mask | 
0 | Metric
…… | 
0 | Metric | 
PrefixLength | PrefixOptions | 0
Address Prefix |  | 
…… |  | 
 | P | MC | LA | MU
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 inter-area-prefix-LSA are described as follows:
  Metric: indicates the cost of the route to the destination address and occupies 3 bytes.
  PrefixOptions: Each prefix advertised by an LSA has its own PrefixOptions field.
    P-bit: propagate bit. This bit needs to be set to 1 if the prefix of an NSSA needs to be advertised by an ABR.
    MC-bit: multicast bit. If this bit is set to 1, the prefix is used for multicast route calculation. Otherwise, the prefix is not used for multicast route calculation.
    LA-bit: local address capability bit. If this bit is set to 1, the prefix is an interface address of the router.
    NU-bit: no unicast capability bit. If this bit is set to 1, the prefix is not used for IPv6 unicast route calculation.
Note: The prefix length of the default route is 0. An ABR can also originate an inter-area Type 3 LSA to advertise a default route to a stub area.

## Slide 30: Type 4: Inter-Area-Router-LSA
OSPFv2: ASBR-summary-LSA
OSPFv3
Similar to a Type 4 LSA in OSPFv2, a Type 4 LSA in OSPFv3 is generated by an ABR, describes the route to an ASBR, and is advertised to areas excluding that to which the ASBR belongs. An ABR sends a Type 4 LSA to describe each ASBR.
Description of key fields:
  Destination Router ID: indicates the router ID of the destination router being described by the LSA, that is, the router ID of an ASBR. This field occupies 4 bytes.
Network Mask | 
0 | Metric
…… | 
0 | Options
0 | Metric
Destination Router ID | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 inter-area-router-LSA are described as follows:
  Options: This field describes the optional capabilities supported by the destination router instead of those supported by the source router. Therefore, the value of this field should equal that of the Options field in the router-LSA generated by the destination router.
  Metric: indicates the cost of the route to the destination address and occupies 3 bytes.

## Slide 31: Type 5: AS-External-LSA
OSPFv2
OSPFv3
Similar to a Type 5 LSA in OSPFv2, a Type 5 LSA in OSPFv3 is generated by an ASBR, describes the route with a prefix outside the local AS, and is advertised to all areas except the stub area and NSSA.
Description of key fields:
  Referenced LS Type: indicates whether the LSA needs to reference another LSA and occupies 2 bytes.
    0: does not reference any other LSA.
    1: references a router-LSA.
    2: references a network-LSA.
Network Mask |  | 
E | 0 | Metric
Forwarding Address |  | 
External Route Tag |  | 
…… |  | 
0 | E | F | T | Metric | 
PrefixLength |  |  |  | PrefixOptions | Referenced LS Type
Address Prefix |  |  |  |  | 
Forwarding Address (Optional) |  |  |  |  | 
External Route Tag (Optional) |  |  |  |  | 
Referenced Link State ID (Optional) |  |  |  |  | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 AS-external-LSA are described as follows:
  Bit E: indicates the cost type of an AS external route and occupies 1 bit.
    The value 1 indicates the cost of a Type 2 external route. This cost does not increase during route transmission.
    The value 0 indicates the cost of a Type 1 external route. This cost increases during route transmission.
  Bit F: occupies 1 bit. The value 1 indicates that the Forwarding Address field (optional) is included.
  Bit T: occupies 1 bit. The value 1 indicates that the External Route Tag field (optional) is included.
  Metric: indicates the cost of the route to the destination address and occupies 3 bytes.
  PrefixLength, PrefixOptions, and Address Prefix are triplets that describe a prefix and have the same meanings as those in an inter-area-prefix-LSA.
  Forwarding Address: is an optional 128-bit IPv6 address and occupies 4 bytes. This field is included if bit F is 1. In this case, a data packet needs to be forwarded to this address before reaching its destination.
  External Route Tag: an optional flag, which occupies 4 bytes. It can be used for communication between ASBRs. In a typical scenario where each of two ASBRs imports an AS external route, the imported routes can be tagged differently to facilitate route filtering.
  Referenced Link State ID: occupies 4 bytes. This field is included if the Referenced LS Type field is not 0, indicating the link state ID of the referenced LSA.

## Slide 32: Type 8: Link-LSA (Added in OSPFv3)
Link-LSA format
Each device generates a link-LSA for each attached link and floods the link-LSA only on the originating link.
Link-LSA functions:
  Advertises the link-local address of the local interface to other routers attached to the originating link.
  Advertises a list of IPv6 prefixes of the local interface to other routers attached to the originating link.
  Advertises a collection of Options bits in the network-LSA originated on the local link to other routers attached to the originating link.
Description of key fields:
  Link-Local Interface Address: indicates the link-local address of the interface that connects the originating router to the link, and occupies 16 bytes. This address is contained only in the Link-LSA.
Rtr Pri | Options | 
Link-Local Interface Address |  | 
Number of prefixes |  | 
PrefixLength | PrefixOptions | 0
Address Prefix …… |  | 
…… |  | 
PrefixLength | PrefixOptions | 0
Address Prefix …… |  | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 link-LSA are described as follows:
  Rtr Pri: indicates the router priority of the interface attaching the originating router to the link and occupies 1 byte.
  Options: indicates a collection of Options bits that the router sets in the network-LSA and occupies 3 bytes.
  Number of Prefixes: indicates the number of IPv6 address prefixes carried in the LSA, and occupies 4 bytes.
  PrefixLength, PrefixOptions, and Address Prefix are triplets that describe a prefix and have the same meanings as those in an inter-area-prefix-LSA.

## Slide 33: Type 9: Intra-Area-Prefix-LSA (Added in OSPFv3)
Intra-area-prefix-LSA format
In OSPFv2, Type 1 and Type 2 LSAs can be used to describe topology and network segment information. In OSPFv3, however, these two types of LSAs contain only topology information. How does OSPFv3 describe network segment information?
Type 9 LSAs describe network segment information and are flooded only in the area to which the originating router belongs. OSPFv3 depends on both Type 9 LSAs and topology information to calculate OSPFv3 routes. Type 9 LSAs have the following two functions:
  Type 9 LSAs generated by each device describe the IPv6 address prefixes associated with router-LSAs.
  Type 9 LSAs generated by a DR describe the IPv6 address prefixes associated with network-LSAs.
Number of Prefixes |  | Referenced LS Type
Referenced Link State ID |  | 
Referenced Advertising Router |  | 
PrefixLength | PrefixOptions | Metric
Address Prefix …… |  | 
…… |  | 
Overview
Implementation
Packets
LSAs
Notes: The fields in an OSPFv3 intra-area-prefix-LSA are described as follows:
  Number of Prefixes: indicates the number of IPv6 address prefixes carried in the LSA, and occupies 4 bytes. If necessary, prefixes can be carried in multiple intra-area-prefix-LSAs to limit the size of each Type 9 LSA.
  Referenced LS Type: indicates whether the LSA references a router-LSA or a network-LSA, and occupies 4 bytes.
    Type=1: A router-LSA is referenced.
    Type=2: A network-LSA is referenced.
  Referenced Link State ID: 4 bytes.
    If the LSA references a router-LSA, this field is set to 0.
    If the LSA references a network-LSA, this field is set to the interface ID of the DR on the attached link.
  Referenced Advertising Router: 4 bytes.
    If the LSA references a router-LSA, this field is set to the router ID of the associated router.
    If the LSA references a network-LSA, this field is set to the router ID of the DR on the attached link.
  PrefixLength, PrefixOptions, and Address Prefix are triplets that describe a prefix and have the same meanings as those in an inter-area-prefix-LSA.
  Metric: indicates the prefix cost and occupies 2 bytes. This field has the same unit as the interface cost of a router-LSA.
In OSPFv3, when a link or its prefix changes, the attached router sends an intra-area-prefix-LSA, which however does not trigger SPF calculation.

## Slide 34: Examples of OSPFv3 LSAs
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/1 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 2001:DB8:2345:23::3/64
R4 | 10.1.4.4 | GE0/0/2 | 2001:DB8:2345:23::4/64
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
[R2]display ospfv3 lsdb
* indicates STALE LSA
OSPFv3 Router with ID (10.1.2.2) (Process 1)
Link-LSA (Interface GigabitEthernet0/0/0)
Link State ID Origin Router Age Seq# CkSum Prefix
0.0.0.3 10.1.2.2 0080 0x80000002 0x1c52 1
0.0.0.4 10.1.3.3 0075 0x80000002 0x2a59 1
0.0.0.5 10.1.4.4 0089 0x80000002 0xe2a3 1
Link-LSA (Interface GigabitEthernet0/0/1)
Link State ID Origin Router Age Seq# CkSum Prefix
0.0.0.4 10.1.1.1 0070 0x80000002 0xe971 1
0.0.0.4 10.1.2.2 0069 0x80000002 0x9fdd 1
Router-LSA (Area 0.0.0.0)
……
Network-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum
0.0.0.4 10.1.2.2 0030 0x80000001 0x9564
0.0.0.5 10.1.4.4 0036 0x80000002 0xc810
Intra-Area-Prefix-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum Prefix Reference
0.0.0.1 10.1.2.2 0028 0x80000006 0x1527 1 Network-LSA
0.0.0.1 10.1.4.4 0034 0x80000003 0xfc28 1 Network-LSA
Type 8 LSA
Type 9 LSA
Overview
Implementation
Packets
LSAs
Notes: As shown in the figure, R1, R2, R3, and R4 run OSPFv3 and are all deployed in the backbone area.
After the network becomes stable, check the LSDB of R2. The command output shows information about the following types of LSAs: router-LSA (Type 1), network-LSA (Type 2), Link-LSA (Type 8), and intra-area-prefix-LSA (Type 9).

## Slide 35: Link-LSA Example
Check the link-LSA with the Link State ID of 0.0.0.5 on R2. The command output is as follows:
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/1 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 2001:DB8:2345:23::3/64
R4 | 10.1.4.4 | GE0/0/2 | 2001:DB8:2345:23::4/64
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
[R2]display ospfv3 lsdb link 0.0.0.5
OSPFv3 Router with ID (10.1.2.2) (Process 1)
Link-LSA (Interface GigabitEthernet0/0/0)
LS Age: 446
LS Type: Link-LSA
Link State ID: 0.0.0.5
Originating Router: 10.1.4.4
LS Seq Number: 0x80000002
Retransmit Count: 0
Checksum: 0xE2A3
Length: 56
Priority: 1
Options: 0x000013 (-|R|-|-|E|V6)
Link-Local Address: FE80::2E0:FCFF:FEAC:6C5
Number of Prefixes: 1
Prefix: 2001:DB8:2345:23::/64
Prefix Options: 0 (-|-|-|-|-)
Link-local address
Type 8 LSA
IPv6 address prefix of the network segment where the physical interface resides
Overview
Implementation
Packets
LSAs
Notes: The command output is described as follows:
  LS Age: aging time of the LSA.
  LS Type: LSA type, which can be any of the following:
    Router-LSA, Network-LSA, Inter-Area-Prefix-LSA, Inter-Area-Router-LSA, AS-external-LSA, NSSA-LSA, Link-LSA, or Intra-Area-Prefix-LSA
  Link State ID: link state ID in the LSA header.
  Originating Router: router that generates the LSA.
  LS Seq Number: sequence number of the LSA. This field is carried in the LSA header.
  Checksum: checksum of the LSA.
  Length: length of the LSA.
  Priority: priority of the interface attached to the link.
  Options: optional capabilities of the link.
  Link-Local Address: link-local address.
  Number of Prefixes: number of IPv6 prefixes contained in the LSA.
  Prefix: IPv6 prefix.
  Prefix Options: optional capabilities associated with the prefix.

## Slide 36: Intra-Area-Prefix-LSA Example
Check the intra-area-prefix-LSA on R2. The command output is as follows:
Device | Router ID | Interface | IP Address
R1 | 10.1.1.1 | GE0/0/1 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 2001:DB8:2345:23::3/64
R4 | 10.1.4.4 | GE0/0/2 | 2001:DB8:2345:23::4/64
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
[R2]display ospfv3 lsdb intra-prefix
OSPFv3 Router with ID (10.1.2.2) (Process 1)
Intra-Area-Prefix-LSA (Area 0.0.0.0)
……
LS Age: 556
LS Type: Intra-Area-Prefix-LSA
Link State ID: 0.0.0.1
Originating Router: 10.1.4.4
LS Seq Number: 0x80000003
Retransmit Count: 0
Checksum: 0xFC28
Length: 44
Number of Prefixes: 1
Referenced LS Type: 0x2002
Referenced Link State ID: 0.0.0.5
Referenced Originating Router: 10.1.4.4
Prefix: 2001:DB8:2345:23::/64
Prefix Options: 0 (-|-|-|-|-)
Metric: 0
Reference the network-LSA generated by the DR (R4)
Type 9 LSA
IPv6 address prefix of the transit network segment to which the local router is directly connected. This LSA is generated by the DR.
Overview
Implementation
Packets
LSAs

## Slide 37
IPv6 Static Routes
OSPFv3 Implementation and Configurations
  OSPFv3 Implementation
  Basic OSPFv3 Configurations
IS-IS (IPv6) Implementation and Configurations
BGP4+ Implementation and Configurations

## Slide 38: Basic OSPFv3 Configuration Commands (1)
Start OSPFv3.
An OSPFv3 process is created and runs, and (optional) the process is bound to a VPN instance.
A router ID is configured for the local device in this OSPFv3 process.
Note: If no router ID is configured, the OSPFv3 process cannot run.
Enable OSPFv3 on an interface.
The interface is enabled in the specified OSPFv3 process, and the area to which the interface belongs is specified. You can also specify the ID of the instance to which the interface belongs.
Note: Before running this command, you must create an OSPFv3 process and enable the IPv6 function.
[Huawei] ospfv3 [ process-id ] [ vpn-instance vpn-instance-name ]
[Huawei-ospfv3-1] router-id router-id
[Huawei-GigabitEthernet0/0/1] ospfv3 process-id area area-id [ instance instance-id ]
Notes: The configuration commands and methods of OSPFv3 are similar to those of OSPFv2. For details, see the "HCIP-Datacom-Core Technology" course.

## Slide 39: Basic OSPFv3 Configuration Commands (2)
(Optional) Configure an OSPFv3 network type for the interface.
By default, the OSPFv3 network type of a physical interface depends on the data link layer encapsulation of the interface. The default network type of an Ethernet interface is broadcast, whereas that of a serial interface (encapsulated with PPP or HDLC) is P2P.
Enter the OSPFv3 area view.
The specified area ID can be a decimal integer or in the IPv4 address format. Regardless of the specified format, the area ID is displayed as an IPv4 address.
[Huawei-GigabitEthernet0/0/1] ospfv3 network-type { broadcast | nbma | p2mp [ non-broadcast ] | p2p } [ instance instance-id ]
[Huawei-ospfv3-1] area area-id

## Slide 40: Verifying the Configuration of Basic OSPFv3 Functions
Check the OSPFv3 interface information.
Check the OSPFv3 neighbor information.
neighbor-id: specifies the router ID of a neighbor.
Check the OSPFv3 LSDB.
Check the OSPFv3 routing table.
[Huawei] display ospfv3 [ process-id ] interface [ area area-id ] [ interface-type interface-number ]
[Huawei] display ospfv3 [ process-id ] [ area area-id ] peer [ interface-type interface-number | neighbor-id ] [ verbose ]
[Huawei] display ospfv3 [ process-id ] lsdb [ area area-id ] [ originate-router advertising-router-id | self-originate ] [ { router | network | inter-router [ asbr-router asbr-router-id ] | { inter-prefix | nssa } [ ipv6-address prefix-length ] | link | intra-prefix } [ link-state-id ] ]
[Huawei] display ospfv3 [ process-id ] routing [ ipv6-address prefix-length | abr-routes | asbr-routes | intra-routes | inter-routes | ase-routes | nssa-routes | [ statistics ] ]
Notes: [Huawei] display ospfv3 [ process-id ] lsdb [ area area-id ] [ originate-router advertising-router-id | self-originate ] [ { router | network | inter-router [ asbr-router asbr-router-id ] | { inter-prefix | nssa } [ ipv6-address prefix-length ] | link | intra-prefix | grace } [ link-state-id ]]
  process-id: specifies the ID of an OSPFv3 process. The value is an integer ranging from 1 to 65535.
  area area-id: specifies the ID of an area. The area ID can be a decimal integer or in the IPv4 address format. For a decimal integer, the value ranges from 0 to 4294967295. For the IPv4 address format, the value is in dotted decimal notation.
  external: displays information about AS-external LSAs in the LSDB.
  inter-prefix: displays information about inter-area-prefix LSAs in the LSDB.
  inter-router: displays information about inter-area-router LSAs in the LSDB.
  intra-prefix: displays information about intra-area-prefix LSAs in the LSDB.
  nssa: displays information about NSSA LSAs in the LSDB.
  link: displays information about link-LSAs in the LSDB.
  network: displays information about network-LSAs in the LSDB.
  router: displays information about router-LSAs in the LSDB.
  link-state-id: specifies a link state ID. The value is in dotted decimal notation.

## Slide 41
Notes:   originate-router advertising-router-id: specifies the router ID of the router that advertises LSAs. The value is in dotted decimal notation.
  asbr-router asbr-router-id: specifies the router ID of an ASBR. The value is in dotted decimal notation.
  self-originate: displays information about the LSAs advertised by the local router in the LSDB.
  ipv6-address prefix-length: specifies the destination IPv6 address and prefix length.
    ipv6-address: The value is a 32-digit hexadecimal number, in the format of X:X:X:X:X:X:X:X.
    prefix-length: The value is an integer ranging from 0 to 128.
[Huawei] display ospfv3 [ process-id ] routing [ ipv6-address prefix-length | abr-routes | asbr-routes | intra-routes | inter-routes | ase-routes | nssa-routes | [ statistics ] ]
  process-id: specifies the ID of an OSPFv3 process. The value is an integer ranging from 1 to 65535.
  ipv6-address: specifies an IPv6 address. The value is a 32-digit hexadecimal number, in the format of X:X:X:X:X:X:X:X.
  prefix-length: specifies a prefix length. The value is an integer ranging from 0 to 128.
  abr-routes: displays information about routes of all ABRs in the OSPFv3 process.
  asbr-routes: displays information about routes of all ASBRs in the OSPFv3 process.
  intra-routes: displays statistics about intra-area routes in the OSPFv3 process.
  inter-routes: displays statistics about inter-area routes in the OSPFv3 process.
  ase-routes: displays statistics about AS external routes in the OSPFv3 process.
  nssa-routes: displays statistics about NSSA routes in the OSPFv3 process.
  statistics: displays statistics of all OSPFv3 routing tables.

## Slide 42: Example for Configuring OSPF IPv4/IPv6 Dual Stack
Scenario description:
  A company has OSPFv2 deployed over an IPv4 network to implement interconnection and communication. To ensure future service development, the company has an IPv6 network deployed for service testing. OSPFv3 runs on the IPv6 network to implement IPv6 interconnection and communication.
  Each router runs both OSPFv2 and OSPFv3, and the entire AS is divided into three areas. After the configuration is complete, each router should learn the IPv4 and IPv6 routes to all network segments in the AS.
Device | Router ID | Interface | IPv4 Address | IPv6 Address
R1 | 10.1.1.1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 10.1.23.2/24 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 10.1.23.3/24 | 2001:DB8:2345:23::3/64
 |  | GE0/0/2 | 10.1.35.3/24 | 2001:DB8:2345:35::3/64
R4 | 10.1.4.4 | GE0/0/2 | 10.1.23.4/24 | 2001:DB8:2345:23::4/64
R5 | 10.1.5.5 | GE0/0/2 | 10.1.35.5/24 | 2001:DB8:2345:35::5/64
R1
R2
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
R3
R4

## Slide 43: Deploying the IPv4 Network (1)
1. Assign an IPv4 address to each router interface. (The configuration details are not provided here.)
2. Configure basic OSPF functions.
Device | Router ID | Interface | IPv4 Address | IPv6 Address
R1 | 10.1.1.1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 10.1.23.2/24 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 10.1.23.3/24 | 2001:DB8:2345:23::3/64
 |  | GE0/0/2 | 10.1.35.3/24 | 2001:DB8:2345:35::3/64
R4 | 10.1.4.4 | GE0/0/2 | 10.1.23.4/24 | 2001:DB8:2345:23::4/64
R5 | 10.1.5.5 | GE0/0/2 | 10.1.35.5/24 | 2001:DB8:2345:35::5/64
R1
R2
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
R3
R4
[R1] ospf 1 router-id 10.1.1.1
[R1-ospf-1] area 1
[R1-ospf-1-area-0.0.0.1] network 10.1.12.1 0.0.0.0
[R2] ospf 1 router-id 10.1.2.2
[R2-ospf-1] area 1
[R2-ospf-1-area-0.0.0.1] network 10.1.12.2 0.0.0.0
[R2-ospf-1-area-0.0.0.1] quit
[R2-ospf-1] area 0
[R2-ospf-1-area-0.0.0.0] network 10.1.23.2 0.0.0.0
[R3] ospf 1 router-id 10.1.3.3
[R3-ospf-1] area 0
[R3-ospf-1-area-0.0.0.0] network 10.1.23.3 0.0.0.0
[R3-ospf-1-area-0.0.0.0] quit
[R3-ospf-1] area 2
[R3-ospf-1-area-0.0.0.2] network 10.1.35.3 0.0.0.0

## Slide 44: Deploying the IPv4 Network (2)
Device | Router ID | Interface | IPv4 Address | IPv6 Address
R1 | 10.1.1.1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 10.1.23.2/24 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 10.1.23.3/24 | 2001:DB8:2345:23::3/64
 |  | GE0/0/2 | 10.1.35.3/24 | 2001:DB8:2345:35::3/64
R4 | 10.1.4.4 | GE0/0/2 | 10.1.23.4/24 | 2001:DB8:2345:23::4/64
R5 | 10.1.5.5 | GE0/0/2 | 10.1.35.5/24 | 2001:DB8:2345:35::5/64
R1
R2
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
R3
R4
[R4] ospf 1 router-id 10.1.4.4
[R4-ospf-1] area 0
[R4-ospf-1-area-0.0.0.0] network 10.1.23.4 0.0.0.0
[R5] ospf 1 router-id 10.1.5.5
[R5-ospf-1] area 2
[R5-ospf-1-area-0.0.0.2] network 10.1.35.5 0.0.0.0

## Slide 45: Deploying the IPv6 Network (1)
1. Enable IPv6 globally and on interfaces, and assign IPv6 addresses to interfaces on each router. (The configuration details are not provided here.)
2. Enable OSPFv3.
Device | Router ID | Interface | IPv4 Address | IPv6 Address
R1 | 10.1.1.1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 10.1.23.2/24 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 10.1.23.3/24 | 2001:DB8:2345:23::3/64
 |  | GE0/0/2 | 10.1.35.3/24 | 2001:DB8:2345:35::3/64
R4 | 10.1.4.4 | GE0/0/2 | 10.1.23.4/24 | 2001:DB8:2345:23::4/64
R5 | 10.1.5.5 | GE0/0/2 | 10.1.35.5/24 | 2001:DB8:2345:35::5/64
R1
R2
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
R3
R4
[R1] ospfv3 1
[R1-ospfv3-1] router-id 10.1.1.1
[R2] ospfv3 1
[R2-ospfv3-1] router-id 10.1.2.2
[R3] ospfv3 1
[R3-ospfv3-1] router-id 10.1.3.3
[R4] ospfv3 1
[R4-ospfv3-1] router-id 10.1.4.4
[R5] ospfv3 1
[R5-ospfv3-1] router-id 10.1.5.5

## Slide 46: Deploying the IPv6 Network (2)
3. Enable OSPFv3 on interfaces.
Device | Router ID | Interface | IPv4 Address | IPv6 Address
R1 | 10.1.1.1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
R2 | 10.1.2.2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 |  | GE0/0/0 | 10.1.23.2/24 | 2001:DB8:2345:23::2/64
R3 | 10.1.3.3 | GE0/0/1 | 10.1.23.3/24 | 2001:DB8:2345:23::3/64
 |  | GE0/0/2 | 10.1.35.3/24 | 2001:DB8:2345:35::3/64
R4 | 10.1.4.4 | GE0/0/2 | 10.1.23.4/24 | 2001:DB8:2345:23::4/64
R5 | 10.1.5.5 | GE0/0/2 | 10.1.35.5/24 | 2001:DB8:2345:35::5/64
R1
R2
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
R3
R4
[R1] interface gigabitethernet 0/0/1
[R1-GigabitEthernet0/0/1] ospfv3 1 area 1
[R2] interface gigabitethernet 0/0/1
[R2-GigabitEthernet0/0/1] ospfv3 1 area 1
[R2-GigabitEthernet0/0/1] quit
[R2] interface gigabitethernet 0/0/0
[R2-GigabitEthernet0/0/0] ospfv3 1 area 0
[R3] interface gigabitethernet 0/0/1
[R3-GigabitEthernet0/0/1] ospfv3 1 area 0
[R3-GigabitEthernet0/0/1] quit
[R3] interface gigabitethernet 0/0/2
[R3-GigabitEthernet0/0/2] ospfv3 1 area 2
[R4] interface gigabitethernet 0/0/2
[R4-GigabitEthernet0/0/2] ospfv3 1 area 0
[R5] interface gigabitethernet 0/0/2
[R5-GigabitEthernet0/0/2] ospfv3 1 area 2

## Slide 47: Checking Neighbor Information on the OSPFv3 Network
[R2]display ospfv3 peer
OSPFv3 Process (1)
OSPFv3 Area (0.0.0.0)
Neighbor ID Pri State Dead Time Interface Instance ID
10.1.3.3 1 Full/Backup 00:00:31 GE0/0/0 0
10.1.4.4 1 Full/DR 00:00:36 GE0/0/0 0
OSPFv3 Area (0.0.0.1)
Neighbor ID Pri State Dead Time Interface Instance ID
10.1.1.1 1 Full/Backup 00:00:37 GE0/0/1 0
If no instance ID is specified, the default value 0 is used.
The instance IDs of the directly connected interfaces on the two devices must be the same. Otherwise, the OSPFv3 neighbor relationship cannot be established.
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
Notes: You can run the display ospf peer command to check OSPFv2 neighbor information.
By comparing OSPFv2 neighbor information and OSPFv3 neighbor information, you will find that the elected DR and BDR are the same, indicating that the DR election modes between OSPFv2 and OSPFv3 are the same.

## Slide 48: Checking the Routing Information on the OSPFv3 Network
[R2]display ospfv3 routing
Codes : E2 - Type 2 External, E1 - Type 1 External, IA - Inter-Area, N - NSSA, U - Uninstalled
OSPFv3 Process (1)
Destination Metric Next-hop
2001:DB8:2345:12::/64 1 directly connected, GigabitEthernet0/0/1
2001:DB8:2345:23::/64 1 directly connected, GigabitEthernet0/0/0
IA 2001:DB8:2345:35::/64 2 via FE80::2E0:FCFF:FE38:50A0, GigabitEthernet0/0/0
In OSPFv3, the next-hop address of a route is a link-local address.
The next-hop address of this route is the link-local address of R3's GE0/0/1.
R1
R2
R3
R4
GE0/0/1
GE0/0/1
GE0/0/0
GE0/0/1
GE0/0/2
GE0/0/2
R5
Area 1
Area 0
Area 2
2001:D88:2345:12::/64
2001:D88:2345:23::/64
2001:D88:2345:35::/64
Notes: You can run the display ospf routing command to check the routing information on the OSPFv2 network.
By comparing OSPFv2 routing information and OSPFv3 routing information, you will find that the paths to the same network segment are the same, indicating that the route calculation methods between OSPFv2 and OSPFv3 are the same.

## Slide 49: Checking the LSDB on the OSPFv3 Network
The LSDB on R2 contains the Type 1, Type 2, Type 3, Type 8, and Type 9 LSAs.
[R2]display ospfv3 lsdb
* indicates STALE LSA
OSPFv3 Router with ID (10.1.2.2) (Process 1)
Link-LSA (Interface GigabitEthernet0/0/0)
Link State ID Origin Router Age Seq# CkSum Prefix
0.0.0.3 10.1.2.2 0862 0x80000003 0x486d 1
0.0.0.4 10.1.3.3 0854 0x80000003 0xc512 1
0.0.0.5 10.1.4.4 0840 0x80000003 0x4e3c 1
Link-LSA (Interface GigabitEthernet0/0/1)
Link State ID Origin Router Age Seq# CkSum Prefix
0.0.0.4 10.1.1.1 0878 0x80000003 0x9d8f 1
0.0.0.4 10.1.2.2 0868 0x80000003 0xcbf8 1
Router-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum Link
0.0.0.0 10.1.2.2 0567 0x8000000f 0xd411 1
0.0.0.0 10.1.3.3 0576 0x8000000e 0xd70c 1
0.0.0.0 10.1.4.4 0577 0x8000000a 0xdd08 1
Network-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum
0.0.0.5 10.1.4.4 0577 0x80000006 0xc014
Inter-Area-Prefix-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum
0.0.0.1 10.1.2.2 0862 0x80000003 0xceb3
0.0.0.1 10.1.3.3 0782 0x80000004 0x3824
Intra-Area-Prefix-LSA (Area 0.0.0.0)
Link State ID Origin Router Age Seq# CkSum Prefix Reference
0.0.0.1 10.1.4.4 0576 0x8000000a 0xee2f 1 Network-LSA
Router-LSA (Area 0.0.0.1)
Link State ID Origin Router Age Seq# CkSum Link
0.0.0.0 10.1.1.1 0819 0x80000007 0x9460 1
0.0.0.0 10.1.2.2 0827 0x80000007 0x8a67 1
Network-LSA (Area 0.0.0.1)
Link State ID Origin Router Age Seq# CkSum
0.0.0.4 10.1.2.2 0828 0x80000003 0x9166
Inter-Area-Prefix-LSA (Area 0.0.0.1)
Link State ID Origin Router Age Seq# CkSum
0.0.0.1 10.1.2.2 0570 0x80000001 0x510f
0.0.0.2 10.1.2.2 0596 0x80000001 0xfb76
Intra-Area-Prefix-LSA (Area 0.0.0.1)
Link State ID Origin Router Age Seq# CkSum Prefix Reference
0.0.0.1 10.1.2.2 0826 0x80000004 0x1925 1 Network-LSA
Notes: You can run the display ospf lsdb command to check the OSPFv2 LSDB. You will find that the LSDB contains the Type 1, Type 2, and Type 3 LSAs.

## Slide 50
IPv6 Static Routes
OSPFv3 Implementation and Configurations
IS-IS (IPv6) Implementation and Configurations
BGP4+ Implementation and Configurations

## Slide 51: IS-IS (IPv6) Overview
IS-IS is a link-state dynamic routing protocol, which was initially designed for the OSI network. Later, to support IPv4 routing, extensions were made to apply IS-IS to IPv4 networks. This is called integrated IS-IS.
IS-IS packets are classified into Hello protocol data units (PDUs), link state PDUs (LSPs), and sequence number PDUs (SNPs).
  Packet format
  The Variable Length Fields (TLV) part consists of multiple TLV triplets. Using the TLV structure to construct packets improves the flexibility and scalability of IS-IS. To support new features, only new TLVs need to be added.
To support the processing and calculation of IPv6 routes, two TLVs and one network layer protocol identifier (NLPID) are added to IS-IS.
PDU Common Header
PDU Specific Header
Variable Length Fields (TLV)
Type
Length
Value

## Slide 52: New TLVs
TLV 232 (IPv6 Interface Address)
It is equivalent to TLV 132 (used to describe IPv4 interface addresses). The only difference is that TLV 232 describes 128-bit IPv6 addresses instead of 32-bit IPv4 addresses.
The content of the Interface Address field varies according to different types of PDUs:
For Hello PDUs, the Interface Address TLVs can contain only the link-local IPv6 addresses assigned to the interfaces that send the Hello PDUs.
For LSPs, the Interface Address TLVs can contain only the non-link-local IPv6 addresses assigned to the device interfaces.
TLV 236 (IPv6 Reachability)
It is equivalent to TLVs 128 and 130, and uses the X-bit to identify internal or external reachability information.
The IPv6 Reachability TLV describes the IPv6 network prefix and path cost that are reachable to the source router.
The IPv6 Reachability TLV may appear any number of times (including 0) within an LSP. Link-local prefixes are not advertised using this TLV.
Type=232 | Length | Interface Address 1
Interface Address 1 |  | 
Interface Address 1 |  | 
Interface Address 1 |  | 
Interface Address 1 |  | Interface Address 2
…… |  | 
Type=236 | Length | Metric |  |  |  | 
Metric |  | U | X | S | R | Prefix Length
Prefix |  |  |  |  |  | 
Sub-TLV Len | Sub-TLV |  |  |  |  | 
Notes: Fields in TLV 232 (IPv6 Interface Address) are described as follows:
  Type: indicates the TLV type and occupies 8 bits. The value is 232 (0xE8).
  Length: indicates the length of the Value field in the TLV and occupies 8 bits.
  Interface Address: indicates a 128-bit IPv6 address.
Fields in TLV 236 (IPv6 Reachability) are described as follows:
  Type: indicates the TLV type and occupies 8 bits. The value is 236 (0xEC).
  Length: indicates the length of the Value field in the TLV and occupies 8 bits.
  Metric: a 32-bit field indicating the cost.
  U: up/down bit. This 1-bit field indicates whether the prefix is advertised from a higher level to a lower level.
  X: external original bit. This 1-bit field indicates whether the prefix was imported into IS-IS from another routing protocol.
  S: sub-TLV present bit. This 1-bit field is optional.
  R: This 5-bit field is reserved.
  Prefix Length: indicate the prefix length and occupies 8 bits.
  Prefix: indicates an IPv6 address prefix.
  Sub-TLV Length: indicates the length of a sub-TLV and occupies 8 bits. If the S-bit is set to 1, this field is included.
  Sub-TLV: If the S-bit is set to 1, this field is included.

## Slide 53: New NLPID in TLV 129
To support the processing and calculation of IPv6 routes, IS-IS adds an NLPID to TLV 129.
TLV 129 (Protocol Supported)
Field description:
Type: indicates the TLV type and occupies 8 bits. The value is 129 (0x81), indicating the Protocol Supported TLV.
Length: indicates the length of the Value field in the TLV and occupies 8 bits.
NLPID: indicates the network layer protocol identifier and occupies 8 bits. If IPv4 is supported, the value is 204 (0xCC). If IPv6 is supported, the value is 142 (0x8E).
If IS-IS supports IPv6, the IPv6 routing information that it advertises must carry the NLPID.
Type=129 | Length | NLPID | NLPID
…… |  |  | 

## Slide 54: IS-IS Multi-Topology Background
By default, on an IS-IS network, a mix of IPv4 and IPv6 topologies is considered as an integrated topology, and IS-IS calculates the same SPT for IPv4 and IPv6.
IS-IS single-topology has the following problems:
  In a mixed topology, routers that support the IPv4/IPv6 dual stack cannot detect the routers or links that do not support IPv6 and may still forward IPv6 packets to them. As a result, the IPv6 packets are discarded due to a forwarding failure.
  Similarly, if routers and links that do not support IPv4 exist in the topology, IPv4 packets are discarded.
Physical topology
IPv6 is not supported.
R1 (IPv4/IPv6)
2
3
IPv4 logical topology
4
5
1
2
3
IPv6 logical topology
4
5
1
IS-IS
R3 does not support IPv6 and discards the IPv6 packets received from R1.
R3 (IPv4)
R4 (IPv4/IPv6)
R5 (IPv4/IPv6)
R2 (IPv4/IPv6)
Notes: IS-IS single-topology has the following disadvantages:
  Network deployment is not suitable for topology separation.
  To maintain the same topology, each interface must run both IS-IS (IPv4) and IS-IS (IPv6), which is not flexible.
  IPv4 areas cannot be used to connect different IPv6 areas. That is, IPv4 networks cannot be used to address IPv6 network isolation.

## Slide 55: IS-IS Multi-Topology Overview
The IS-IS multi-topology (MT) feature indicates that multiple independent IP topologies run in an IS-IS domain. For example, IPv4 and IPv6 topologies are not considered as a single integrated topology. This ensures that IS-IS routes are calculated for both IPv4 and IPv6 networks. Based on the IP versions supported by links, separate SPF calculation is performed in each topology to shield networks from each other.
IS-IS MT implementation
  Topology establishment: Neighbor relationships are established through packet exchange to set up multiple topologies.
  SPF calculation: SPF calculation is performed in each topology.
Notes: The IS-IS MT feature can overcome the disadvantages of IS-IS single topology.

## Slide 56: IS-IS MT Implementation
IS-IS defines new TLVs, which contain MT information, that is, information about the topologies to which interfaces belong. The advertisement of MT information enables the network to perform separate SPF calculations for different topologies, implementing topology separation.
Multi-Topology TLV 229
Key fields are described as follows:
Type: indicates the TLV type and occupies 8 bits. The value is 229 (0xE5), indicating support for MT.
O: Overload bit, which occupies 1 bit.
A: Attach bit, which occupies 1 bit.
MT ID: indicates the topology to which the interface belongs, and occupies 12 bits.
IS-IS calculates a separate topology for each of the IPv4 and IPv6 networks.
Type=229 | Length | O | A | R | MT ID
…… |  |  |  |  | 
2
3
IPv4 logical topology
4
5
1
2
IPv6 logical topology
4
5
1
R3 does not support IPv6 and therefore does not exist in the IPv6 SPT.
Notes: To support MT, IS-IS defines multiple types of TLVs, including Multi-Topology TLV, MT Intermediate Systems TLV, Multi-Topology Reachable IPv4 Prefixes TLV, and Multi-Topology Reachable IPv6 Prefixes TLV. This course focuses on the Multi-Topology TLV and does not elaborate on the other ones.
Multi-Topology TLV:
  This TLV is contained only in IIH PDUs and fragment zero LSPs.
  Reserved MT IDs:
    MT ID=0, equivalent to the standard IPv4 topology.
    MT ID=2, reserved for the IPv6 routing topology.

## Slide 57: Basic IS-IS (IPv6) Configuration Commands
Enable IS-IS (IPv6).
The IPv6 capability is enabled in the IS-IS process.
IS-IS IPv6 is enabled on the interface, and the ID of the IS-IS process to be associated with the interface is specified.
Note: Before running this command, you must enable the IPv6 function on the interface.
Set a cost for the IS-IS interface on the IPv6 network.
By default, the link cost of an IS-IS interface in an IPv6 topology is 10.
[Huawei-isis-1] ipv6 enable [ topology { ipv6 | standard } ]
[Huawei-GigabitEthernet0/0/1] isis ipv6 enable [ process-id ]
[Huawei-GigabitEthernet0/0/1] isis ipv6 cost { cost | maximum } [ level-1 | level-2 ]
Notes: The basic configuration commands and methods of IS-IS (IPv6) are the same as those of IS-IS (IPv4). For details, see the "HCIP-Datacom-Core Technology" course.
[Huawei-isis-1] ipv6 enable [ topology { ipv6 | standard } ]
  topology: sets a network topology type.
  ipv6: sets the topology type to IPv6. That is, the IPv6 capability for the IS-IS process is enabled in an IPv6 topology. Links on the network can be configured as IPv4 or IPv6 links. SPF calculation is performed separately in IPv4 and IPv6 topologies.
  standard: sets the topology type to standard. That is, the IPv6 capability for the IS-IS process is enabled in an integrated topology. A network administrator must ensure that all links on the network support the same topology type. By default, the standard type is used when the IPv6 capability is enabled for an IS-IS process.

## Slide 58
Notes: [ Huawei-GigabitEthernet0/0/1] isis ipv6 cost { cost | maximum } [ level-1 | level-2 ]
  cost: specifies the link cost of an IPv6 interface. The value is an integer that varies according to the following cost styles:
    If the cost style is narrow, narrow-compatible, or compatible, the value ranges from 1 to 63.
    If the cost style is wide or wide-compatible, the value ranges from 1 to 16777214.
    The default value is 10.
  maximum: sets the link cost of an interface to 16777215.
  level-1: sets a cost for a Level-1 link. If no interface level is specified, the link cost set for the interface takes effect for both Level-1 and Level-2.
  level-2: sets a cost for a Level-2 link. If no interface level is specified, the link cost set for the interface takes effect for both Level-1 and Level-2.

## Slide 59: Verifying the Configuration of Basic IS-IS (IPv6) Functions
Check information about the interface with IS-IS (IPv6) enabled.
Check IS-IS (IPv6) neighbor information.
Check IS-IS (IPv6) routing information.
[Huawei] display isis interface interface-type interface-number [ verbose ]
[Huawei] display isis process-id peer [ verbose ]
[Huawei] display isis route [ process-id | vpn-instance vpn-instance-name ] ipv6 [ verbose | [ level-1 | level-2 ] | ipv6-address [ prefix-length ] ]

## Slide 60: Example for Configuring IS-IS IPv4/IPv6 Dual Stack
Scenario description:
  A company has IS-IS deployed over an IPv4 network to implement IPv4 network interconnection. To ensure future service development, the company has an IPv6 network deployed for service testing. In this case, the IPv6 function needs to be enabled in the IS-IS process on the network.
  As device performance varies, link cost modification is required to ensure that IPv4 and IPv6 services are routed through different paths, and IS-IS MT is required to ensure that a separate topology is calculated for the IPv6 network.
  All routers run IS-IS and are all Level-2 routers. The entire network is in area 49.0001. After the configuration is complete, each router should learn the IPv4 and IPv6 routes to all network segments in the AS.
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | GE0/0/2 | 10.1.13.1/24 | 2001:DB8:2345:13::1/64
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | GE0/0/2 | 10.1.24.2/24 | 2001:DB8:2345:24::2/64
R3 | GE0/0/1 | 10.1.34.3/24 | 2001:DB8:2345:34::3/64
 | GE0/0/2 | 10.1.13.3/24 | 2001:DB8:2345:13::3/64
R4 | GE0/0/1 | 10.1.34.4/24 | 2001:DB8:2345:34::4/64
 | GE0/0/2 | 10.1.24.4/24 | 2001:DB8:2345:24::4/64
R1
GE0/0/1
GE0/0/2
IS-IS
Area 49.0001
R2
R3
R4
GE0/0/2
GE0/0/1

## Slide 61: Deploying the IPv4 Network
1. Assign an IPv4 address to each router interface. (The configuration details are not provided here.)
2. Configure basic IS-IS functions.
The configurations of R2, R3, and R4 are similar to the configuration of R1, and are not provided here.
The network entity titles (NETs) are as follows:
R2: 49.0001.0000.0000.0002.00
R3: 49.0001.0000.0000.0003.00
R4: 49.0001.0000.0000.0004.00
R1
GE0/0/1
GE0/0/2
IS-IS (IPv4)
Area 49.0001
R2
R3
R4
GE0/0/2
Cost=10
GE0/0/1
Cost=10
Cost=40
Cost=10
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | GE0/0/2 | 10.1.13.1/24 | 2001:DB8:2345:13::1/64
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | GE0/0/2 | 10.1.24.2/24 | 2001:DB8:2345:24::2/64
R3 | GE0/0/1 | 10.1.34.3/24 | 2001:DB8:2345:34::3/64
 | GE0/0/2 | 10.1.13.3/24 | 2001:DB8:2345:13::3/64
R4 | GE0/0/1 | 10.1.34.4/24 | 2001:DB8:2345:34::4/64
 | GE0/0/2 | 10.1.24.4/24 | 2001:DB8:2345:24::4/64
[R1] isis 1
[R1-isis-1] is-level level-2
[R1-isis-1] network-entity 49.0001.0000.0000.0001.00
#
[R1] interface gigabitethernet 0/0/1
[R1-GigabitEthernet0/0/1] isis enable 1
[R1-GigabitEthernet0/0/1] quit
[R1] interface gigabitethernet 0/0/2
[R1-GigabitEthernet0/0/2] isis enable 1
[R1-GigabitEthernet0/0/2] isis cost 40 level-2

## Slide 62: Deploying the IPv6 Network
1. Assign an IPv6 address to each router interface. (The configuration details are not provided here.)
2. Enable IS-IS (IPv6).
The configurations of R2, R3, and R4 are similar to the configuration of R1, and are not provided here.
R1
GE0/0/1
GE0/0/2
IS-IS (IPv6)
Area 49.0001
R2
R3
R4
GE0/0/2
Cost=40
GE0/0/1
Cost=10
Cost=10
Cost=10
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | GE0/0/2 | 10.1.13.1/24 | 2001:DB8:2345:13::1/64
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | GE0/0/2 | 10.1.24.2/24 | 2001:DB8:2345:24::2/64
R3 | GE0/0/1 | 10.1.34.3/24 | 2001:DB8:2345:34::3/64
 | GE0/0/2 | 10.1.13.3/24 | 2001:DB8:2345:13::3/64
R4 | GE0/0/1 | 10.1.34.4/24 | 2001:DB8:2345:34::4/64
 | GE0/0/2 | 10.1.24.4/24 | 2001:DB8:2345:24::4/64
[R1] isis 1
[R1-isis-1] ipv6 enable topology ipv6
#
[R1] interface gigabitethernet 0/0/1
[R1-GigabitEthernet0/0/1] isis ipv6 enable 1
[R1-GigabitEthernet0/0/1] isis ipv6 cost 40 level-2
[R1-GigabitEthernet0/0/1] quit
[R1] interface gigabitethernet 0/0/2
[R1-GigabitEthernet0/0/2] isis ipv6 enable 1

## Slide 63: Check the Routing Information on the IS-IS (IPv4) Network
The following example uses R1 as the root to calculate the SPT. The IS-IS (IPv4) logical topology is shown in the right figure.
IS-IS (IPv4) logical topology
R1
GE0/0/1
GE0/0/2
R2
R3
R4
GE0/0/2
GE0/0/1
Traffic path from R1 to access the 10.1.34.0/24 network segment
[R1]dis ip routing-table protocol isis
Route Flags: R - relay, D - download to fib
------------------------------------------------------------------------------------------------
Public routing table : ISIS
Destinations : 2 Routes : 2
ISIS routing table status : <Active>
Destinations : 2 Routes : 2
Destination/Mask Proto Pre Cost Flags NextHop Interface
10.1.24.0/24 ISIS-L2 15 20 D 10.1.12.2 GigabitEthernet0/0/1
10.1.34.0/24 ISIS-L2 15 30 D 10.1.12.2 GigabitEthernet0/0/1
ISIS routing table status : <Inactive>
Destinations : 0 Routes : 0
10.1.13.0/24
Cost:40
Cost:10
10.1.24.0/24
10.1.12.0/24
Cost:10
Cost:10
10.1.34.0/24
GE0/0/1
GE0/0/2
GE0/0/2

## Slide 64: Check the Routing Information on the IS-IS (IPv6) Network
The following example uses R1 as the root to calculate the SPT. The IS-IS (IPv6) logical topology is shown in the right figure.
[R1]dis ipv6 routing-table protocol isis
Public Routing Table : ISIS
Summary Count : 2
ISIS Routing Table's Status : < Active >
Summary Count : 2
Destination : 2001:DB8:2345:24:: PrefixLength : 64
NextHop : FE80::2E0:FCFF:FE90:3D3A Preference : 15
Cost : 30 Protocol : ISIS-L2
RelayNextHop : :: TunnelID : 0x0
Interface : GigabitEthernet0/0/2 Flags : D
Destination : 2001:DB8:2345:34:: PrefixLength : 64
NextHop : FE80::2E0:FCFF:FE90:3D3A Preference : 15
Cost : 20 Protocol : ISIS-L2
RelayNextHop : :: TunnelID : 0x0
Interface : GigabitEthernet0/0/2 Flags : D
ISIS Routing Table's Status : < Inactive >
Summary Count : 0
R1
GE0/0/1
GE0/0/2
R2
R3
R4
GE0/0/1
Traffic path from R1 to access the 2001:DB8:2345:24::/64
network segment
2001:DB8:2345:13::/64
Cost:10
Cost:10
2001:DB8:2345:24::/64
2001:DB8:2345:12::/64
Cost:40
GE0/0/1
GE0/0/2
GE0/0/2
GE0/0/1
Cost:10
2001:DB8:2345:34::/64
IS-IS (IPv6) logical topology

## Slide 65
IPv6 Static Routes
OSPFv3 Implementation and Configurations
IS-IS (IPv6) Implementation and Configurations
BGP4+ Implementation and Configurations

## Slide 66: BGP4+ Overview
Traditional BGP-4 can manage only IPv4 unicast routing information. Multiprotocol Extensions for BGP (MP-BGP) can carry routing information for multiple network layer protocols. Currently, MP-BGP uses extended attributes and address families to support IPv6, multicast, and VPN, without changing the messaging and routing mechanisms of BGP-4.
MP-BGP for IPv6 unicast networks is called BGP4+. BGP4+ establishes an independent topology for an IPv6 unicast network and stores routing information in an independent routing table. This ensures that routing information on an IPv4 unicast network is isolated from that on an IPv6 unicast network.
Notes: To support IPv6, BGP needs to map IPv6 routing information to the NLRI attributes.

## Slide 67: Address Families That MP-BGP Supports
MP-BGP uses address families to differentiate network layer protocols. To enable BGP peers to exchange different types of routing information, activating the peers and advertising BGP routes need to be performed in the correct address families.
MP-BGP supports the following address families:
  IPv4 unicast address family
  IPv4 multicast address family
  IPv6 unicast address family
  VPNv4 address family
  VPNv6 address family
  ...
R1
R2
R5
R6
R3
R4
IPv6
IPv6
IPv4
IPv4
IPv4 unicast address family
IPv4 unicast address family
IPv4 unicast address family
IPv6 unicast address family
IBGP
EBGP
EBGP
IPv6 unicast address family
IPv6 unicast address family
Peers on the IPv4 network must be activated in the IPv4 unicast address family, whereas peers on the IPv6 network must be activated in the IPv6 unicast address family.

## Slide 68: BGP Path Attributes
BGP Update messages are used to transmit routing information between peers as well as advertise and withdraw routes.
Update message format:
BGP4+ introduces two NLRI attributes:
  MP_REACH_NLRI: indicates the multiprotocol reachable NLRI, which is used to advertise reachable routes and next hop information.
  MP_UNREACH_NLRI: indicates the multiprotocol unreachable NLRI, which is used to withdraw unreachable routes.
Flags | Type Code
Withdrawn Routes Length (2 bytes)
Withdrawn Routes (N bytes)
Total Path Attribute Length (2 bytes)
Path Attributes (N bytes)
Network Layer Reachability Information (N bytes)
Attr. Type | Attr. Length | Attr. Value
14: MP_REACH_NLRI
15: MP_UNREACH_NLRI
Notes: Update message:
  An Update message can be used to advertise multiple routes with the same path attribute. These routes are stored in the NLRI attribute. An Update message can also carry multiple unreachable routes, which are stored in the Withdrawn Routes field, to instruct peers to withdraw these routes.

## Slide 69: NLRI Attributes
MP_REACH_NLRI format:
To advertise IPv6 routes:
  AFI = 2, SAFI = 1 (unicast), SAFI = 2 (multicast)
  Length of Next Hop Network Address field. Generally, the value is 16, indicating that the next-hop address is the global unicast address of the next hop router.
  Reserved: The field value is fixed at 0.
  Network Layer Reachability Information: length-variable field, which indicates the route prefix and mask information.
MP_UNREACH_NLRI format:
To withdraw IPv6 routes:
  AFI = 2, SAFI = 1 (unicast), SAFI = 2 (multicast)
  The Withdrawn Routes field indicates the prefix and mask information of the routes to be withdrawn.
Address Family Identifier
Subsequent Address Family Identifier
Length of Next Hop Network Address
Network Address of Next Hop
Reserved
Network Layer Reachability Information
Address Family Identifier
Subsequent Address Family Identifier
Withdrawn Routes
Notes: Fields in the MP_REACH_NLRI attribute are described as follows:
  Address Family Information: consists of a 2-byte address family identifier (AFI) and a 1-byte subsequent address family identifier (SAFI).
  Length of Next Hop Network Address: indicates the length of the next-hop address and occupies 1 byte. Generally, the value is 16.
  Network Address of Next Hop: The length is variable and depends on the preceding field. Generally, the value is a global unicast address.
  Reserved: 1 byte. The value must be 0.
  Network Layer Reachability Information: contains information about the routes with the same attributes. The value 0 indicates the default route.
Fields in the MP_UNREACH_NLRI field are described as follows:
  Withdrawn Routes: indicates the routes to be withdrawn. The value is in the <mask length, route prefix> format. If the mask length is 0, the associated route is a default route.

## Slide 70: Basic BGP4+ Configuration Commands
Configure a BGP peer.
An IPv6 peer is created in the BGP view.
Enable the local device to exchange routing information with a specified peer in a BGP-IPv6 address family.
A specified BGP-IPv6 address family is enabled, and its view is displayed.
The local device is enabled to exchange routing information with the specified peer in the BGP-IPv6 address family view.
Configure BGP to import routes.
BGP is configured to import specified routes in the IPv6 routing table to the BGP routing table.
[Huawei-bgp] peer ipv6-address as-number { as-number-plain | as-number-dot }
[Huawei-bgp] ipv6-family [ unicast | vpnv6 | vpn-instance vpn-instance-name ]
[Huawei-bgp-af-ipv6] peer ipv6-address enable
[Huawei-bgp-af-ipv6] network ipv6-address prefix-length [ route-policy route-policy-name ]
Notes: The basic configuration commands and methods of BGP4+ are the same as those of BGP. For details, see the "HCIP-Datacom-Core Technology" course.
[Huawei-bgp] ipv6-family [ unicast | vpnv6 | vpn-instance vpn-instance-name ]
  unicast: enters the IPv6 unicast address family view.
  vpnv6: enters the BGP-VPNv6 address family view.
  vpn-instance vpn-instance-name: associates a specified VPN instance with the IPv6 address family and enters the BGP-VPN instance IPv6 address family view. The value is a string of 1 to 31 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").
[Huawei-bgp-af-ipv6] network ipv6-address prefix-length [ route-policy route-policy-name ]
  ipv6-address: specifies the IPv6 address advertised by BGP. The value is a 32-digit hexadecimal number, in the format of X:X:X:X:X:X:X:X.
  prefix-length: specifies the prefix length of the IPv6 address advertised by BGP. The value is an integer ranging from 0 to 128.
  route-policy route-policy-name: specifies the name of the route-policy applied to route advertisement. The value is a string of 1 to 40 case-sensitive characters. If spaces are used, the string must start and end with double quotation marks (").

## Slide 71: Verifying the Configuration of Basic BGP4+ Functions
Check BGP4+ peer information.
Check BGP4+ routing information.
[Huawei] display bgp ipv6 peer ipv6-address [ verbose ]
[Huawei] display bgp ipv6 routing-table

## Slide 72: Example for Configuring BGP IPv4/IPv6 Dual Stack
Scenario description:
  Two branches of a company communicate with each other through BGP. To ensure future service development, an IPv6 network is deployed in each branch for service testing. In this case, BGP4+ needs to be deployed to implement IPv6 network interworking.
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | Loopback0 | 10.1.1.1/32 | 2001:DB8:2345:1::1/128
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | Loopback0 | 10.1.2.2/32 | 2001:DB8:2345:2::2/128
R1
GE0/0/1
AS 65001
R2
EBGP
GE0/0/1
AS 65002
Router ID：10.1.1.1
Router ID：10.1.2.2

## Slide 73: Deploying the IPv4 Network
1. Assign an IPv4 address to each router interface. (The configuration details are not provided here.)
2. Configure basic BGP functions: establish an EBGP peer relationship.
3. Configure BGP to advertise IPv4 routes.
R1
GE0/0/1
AS 65001
R2
EBGP
GE0/0/1
AS 65002
Router ID：10.1.1.1
Router ID：10.1.2.2
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | Loopback0 | 10.1.1.1/32 | 2001:DB8:2345:1::1/128
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | Loopback0 | 10.1.2.2/32 | 2001:DB8:2345:2::2/128
[R1] bgp 65001
[R1-bgp] router-id 10.1.1.1
[R1-bgp] peer 10.1.12.2 as-number 65002
[R2] bgp 65002
[R2-bgp] router-id 10.1.2.2
[R2-bgp] peer 10.1.12.1 as-number 65001
[R1-bgp] iPv4-family unicast
[R1-bgp-af-ipv4] network 10.1.1.1 32
[R2-bgp] iPv4-family unicast
[R2-bgp-af-ipv4] network 10.1.2.2 32

## Slide 74: Deploying the IPv6 Network
1. Assign an IPv6 address to each router interface. (The configuration details are not provided here.)
2. Configure basic BGP4+ functions: establish an EBGP peer relationship and enable the local device to exchange routing information with the EBGP peer.
3. Configure BGP4+ to advertise IPv6 routes.
R1
GE0/0/1
AS 65001
R2
EBGP
GE0/0/1
AS 65002
Router ID：10.1.1.1
Router ID：10.1.2.2
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | Loopback0 | 10.1.1.1/32 | 2001:DB8:2345:1::1/128
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | Loopback0 | 10.1.2.2/32 | 2001:DB8:2345:2::2/128
[R1] bgp 65001
[R1-bgp] peer 2001:DB8:2345:12::2 as-number 65002
[R1-bgp] iPv6-family unicast
[R1-bgp-af-ipv6] peer 2001:DB8:2345:12::2 enable
[R2] bgp 65002
[R2-bgp] peer 2001:DB8:2345:12::1 as-number 65001
[R2-bgp] iPv6-family unicast
[R2-bgp-af-ipv6] peer 2001:DB8:2345:12::1 enable
[R1-bgp-af-ipv6] network 2001:DB8:2345:1::1 128
[R2-bgp-af-ipv6] network 2001:DB8:2345:2::2 128

## Slide 75: Checking the BGP Peer Information
Run the display bgp [ipv6] peer command to check information about the peers on the IPv4 and IPv6 networks. By comparing the command outputs, you will find that the peer information is basically the same except for the addresses used to establish the peer relationships.
[R1]display bgp peer
BGP local router ID : 10.1.1.1
Local AS number: 65001
Total number of peers: 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
10.1.12.2 4 65002 11 12 0 00:06:49 Established 1
BGP
[R1]display bgp ipv6 peer
BGP local router ID : 10.1.1.1
Local AS number : 65001
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
2001:DB8:2345:12::2 4 65002 14 15 0 00:07:35 Established 1
BGP4+

## Slide 76: Checking the BGP4+ Routing Information
Device | Interface | IPv4 Address | IPv6 Address
R1 | GE0/0/1 | 10.1.12.1/24 | 2001:DB8:2345:12::1/64
 | Loopback0 | 10.1.1.1/32 | 2001:DB8:2345:1::1/128
R2 | GE0/0/1 | 10.1.12.2/24 | 2001:DB8:2345:12::2/64
 | Loopback0 | 10.1.2.2/32 | 2001:DB8:2345:2::2/128
Check the BGP4+ routing table. The command output shows that a total of two valid routes exist.
[R1]display bgp ipv6 routing-table
BGP Local router ID is 10.1.1.1
Status codes: * - valid, > - best, d - damped,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
Total Number of Routes: 2
*> Network : 2001:DB8:2345:1::1 PrefixLen : 128
NextHop : :: LocPrf :
MED : 0 PrefVal : 0
Label :
Path/Ogn : i
*> Network : 2001:DB8:2345:2::2 PrefixLen : 128
NextHop : 2001:DB8:2345:12::2 LocPrf :
MED : 0 PrefVal : 0
Label :
Path/Ogn : 65002 i
R1
GE0/0/1
AS 65001
R2
EBGP
GE0/0/1
AS 65002
Router ID：10.1.1.1
Router ID：10.1.2.2

## Slide 77: Checking the NLRI Attributes of BGP4+
By analyzing the Update message sent by R1, you can check information about the MP_REACH_NLRI attribute. In the attribute:
  Next-hop address of the reachable route: 2001:db8:2345:12::1
  Prefix and prefix length of the reachable route: 2001:db8:2345:1::1/128
UPDATE Message-Border Gateway Protocol
UPDATE Message
Marker: 16 bytes
Length: 85 bytes
Type: UPDATE Message (2)
Unfeasible routes length: 0 bytes
Total path attribute length: 62 bytes
Path attributes
ORIGIN: IGP (4 bytes)
AS_PATH: 65001 (9 bytes)
MULTI_EXIT_DISC: 0 (7 bytes)
MP_REACH_NLRI (42 bytes)
Flags: 0x90 (Optional, Non-transitive, Complete, Extended Length)
Type code: MP_REACH_NLRI (14)
Length: 38 bytes
Address family: IPv6 (2)
Subsequent address family identifier: Unicast (1)
Next hop network address (16 bytes)
Next hop: 2001:db8:2345:12::1 (16)
Subnetwork points of attachment: 0
Network layer reachability information (17 bytes)
2001:db8:2345:1::1/128
MP Reach NLRI prefix length: 128
MP Reach NLRI prefix: 2001:db8:2345:1::1
R1
GE0/0/1
AS 65001
R2
EBGP
GE0/0/1
AS 65002
2001:DB8:2345:12::/64
::1
::2
Loopback0：
2001:DB8:2345:1::1/128

## Slide 78
(Multiple-answer question) Which of the following types of LSAs belong to OSPFv3? ( )
  Router-LSA
  Network-LSA
  Network-summary-LSA
  Link-LSA
(True or false) IS-IS can calculate the SPTs for IPv4 and IPv6 networks separately. ( )
  True
  False
Notes: ABD
A

## Slide 79
IPv6 static routes can meet network interconnection requirements. However, as the network scale expands, dynamic routing protocols need to be leveraged. Dynamic routing protocols are required to support IPv6 and carry IPv6 addresses for route advertisement.
To support IPv6 networks, the IETF enhanced and improved OSPFv2 and finally developed the new protocol, OSPFv3.
IS-IS features high scalability and supports IPv6 through new TLVs.
Similarly, BGP supports IPv6 by using its own extended path attributes and multi-protocol address families.