## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2021.09.15
Wang Xuan/00618840 & Zhu Shigeng/00261992
New
Lu Yueyue/WX445705
2021.10.15
He Junjian/WX580230
Update

## Slide 2: IPv6 Transition Technologies

## Slide 3
As shortage of IPv4 addresses becomes severer, IPv4-to-IPv6 transition has become the focus of network development. Although IPv6 is the ultimate solution to this problem, IPv4 networks will be retained for a long period of time to meet service continuity requirements. During the IPv4-to-IPv6 transition, it is inevitable that IPv4 and IPv6 addresses coexist on networks.
This course describes the transition technologies used when IPv4 and IPv6 coexist, including IPv6 over IPv4 tunneling, IPv6 Provider Edge (6PE), IPv6 VPN Provider Edge (6VPE), IPv4 over IPv6 tunneling, Network Address Translation IPv6-to-IPv4 (NAT64), and IVI.

## Slide 4
On completion of this course, you will be able to:
  Master the basics of IPv6, such as classification and obtaining of IPv6 addresses.
  Describe IPv6 transition technologies and their implementations, and complete the configuration.

## Slide 5
IPv6 Basics
IPv6 Transition Technologies

## Slide 6: Problem Faced by IP Networks and Introduction to IPv6 Technologies
The development of IP networks is driven by services and applications. The IP protocol requires each network terminal to have a unique addressable IP address. The Internet Assigned Numbers Authority (IANA) issued the last five Class A IPv4 address segments in February 2011. This means it has been more difficult to obtain available IPv4 addresses since then.
Currently, IP networks are facing the problem that new services require a large number of IP addresses.
IP technologies have been widely applied due to the great success of the IPv4 Internet. However, with the rapid development of the Internet, IPv4's disadvantages become more apparent:
The IPv4 address space is insufficient.
A large number of routing entries on devices need to be maintained.
Address autoconfiguration and readdressing cannot be easily performed.
IPv6 — resolving the problem of IP address shortage
The most significant difference between IPv6 and IPv4 is that IP addresses are lengthened from 32 bits to 128 bits.
IPv6 is more competitive due to its features such as simplified packet header, sufficient address space, hierarchical address structure, flexible extension header, and enhanced neighbor discovery mechanism.
Notes: Disadvantages of IPv4:
  The IPv4 address space is insufficient. IPv4 addresses are 32 bits long. Theoretically, 4.3 billion IPv4 addresses can be provided. However, the number of IPv4 addresses that are actually available cannot reach this number due to various address assignment reasons. Additionally, IPv4 address resources are unevenly assigned. IPv4 addresses in U.S. account for almost half of all addresses, leaving insufficient addresses for Europe and even fewer for the Asia-Pacific region. The shortage of IPv4 addresses limits further development of mobile IP and broadband technologies that require an increasing number of IP addresses.
  A large number of routing entries on devices need to be maintained. At the initial stage of IPv4 development, many discontinuous IPv4 addresses are assigned. As a result, routes cannot be effectively summarized. The increasingly large routing table consumes a lot of memory resources and affects forwarding efficiency. Device vendors must continually upgrade devices to improve route addressing and forwarding performance.
  Address autoconfiguration and readdressing cannot be easily performed. IPv4 addresses are only 32 bits long, and they are unevenly assigned. As a result, IP addresses need to be reassigned during network expansion or reconstruction, increasing the maintenance workload.
Advantages of IPv6:
  Easy to deploy.
  Compatible with various applications.
  Smooth transition from IPv4 networks to IPv6 networks.

## Slide 7: IPv6 Basics: IPv6 Header
Version | IHL | ToS | Total Len |  | 
Identification |  |  | Flags | Fragment Offset | 
TTL |  | Protocol | Head Checksum |  | 
Source address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Reserved
Removed
Location/Name changed
New
IPv4 header (20–60 octets)
Basic IPv6 header (40 octets)
The checksum at Layer 3 is removed. The checksums at Layer 2 and Layer 4 have been provided in the protocol stack. Therefore, the checksum at Layer 3 is removed to save router processing resources.
The fragmentation function on intermediate nodes is removed. Fragments are processed only on the source node that generates data, but not on intermediate routers. This prevents the intermediate routers from consuming a large amount of CPU resources to process fragments.
The fixed-length IPv6 header is defined. This facilitates fast hardware processing and improves the forwarding efficiency of routers.
Security options are supported. IPv6 provides optimal support for IPsec, allowing the upper-layer protocols to omit many security options.
The Flow Label field is added. This improves QoS efficiency.
Improvements of an IPv6 header over an IPv4 header
Notes: The IPv6 header is also called fixed header, which contains eight fields in 40 octets. The fields are Version, Traffic Class, Flow Label, Payload Length, Next Header, Hop Limit, Source Address, and Destination Address.
  Version: This field indicates the version of IP and its value is 6. The length is 4 bits.
  Traffic Class: This field indicates the class or priority of an IPv6 packet and its function is similar to that of the ToS field in an IPv4 header. The length is 8 bits.
  Flow Label: An IPv4 header does not contain this field. It is a new field. It is used by a source to label sequences of packets for which the label requests special handling by IPv6 routers. The length is 20 bits. Generally, the flow label, together with the source and destination IPv6 addresses, can determine a flow.
  Payload Length: This field indicates the length of the IPv6 payload. The payload refers to the extension header and upper-layer protocol data unit that follow the IPv6 header. This field is 16 bits long and can specify a maximum length of 65535 octets for the payload. If the payload size exceeds 65535 octets, the field is set to 0, and the Jumbo Payload option in the Hop-by-Hop Options header is used to express the actual payload length.

## Slide 8
Notes:   Next Header: This field indicates the type of the first extension header (if any) that follows the IPv6 header or the protocol type in the upper-layer protocol data unit. The length is 8 bits.
  Hop Limit: This field is similar to the TTL field in an IPv4 packet. This field defines the maximum allowable number of hops that an IP packet can pass through. The value decrements by 1 each time an IP packet passes through a router. The packet is discarded if Hop Limit decrements to zero. The length of this field is 8 bits.
  Source Address: This field indicates the address of a sender and its length is 128 bits.
  Destination Address: This field indicates the address of a receiver and its length is 128 bits.

## Slide 9: IPv6 Basics: IPv6 Extension Header
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Extension Header Length | 
Extension header 1's data |  | 
Payload (such as TCP/UDP packets)
40 octets
Variable length
Next Header | Extension Header Length | 
Extension header 2's data |  | 
Variable length
Next Header: 8 bits long. This field is similar to the Next Header field in the basic IPv6 header, indicating the next extension header (if any) or upper-layer protocol type.
Extension Header Length: 8 bits long. This field indicates the extension header length excluding the Next Header field.
Extension Header Data: variable length. This field includes a series of options and the padding field.

## Slide 10: IPv6 Basics: IPv6 Address
An IPv6 address is 128 bits long. Generally, an IPv6 address is divided into eight groups by colon, and each group contains 16 bits and is expressed in hexadecimal notation.
IPv6 address format
X:X:X:X:X:X:X:X
An IPv6 address is represented as eight groups of four hexadecimal digits (0 to 9, A to F), each group represented by an "X" and containing 16 bits. The groups are separated by colon (:).
For the convenience of writing, leading zeros in each group can be omitted, and two or more consecutive all-zero groups can be replaced by two colons (::).
For example, 2031:0000:130F:0000:0000:09C0:876A:130B can be written as 2031:0:130F::9C0:876A:130B.
Address structure: network prefix + interface ID
Network prefix: equivalent to the network ID of an IPv4 address, which is of n bits.
Interface ID: equivalent to the host ID of an IPv4 address, which is of (128 – n) bits.
IPv6 address classification
Unicast address
Global unicast address (GUA): It is equivalent to a public IPv4 address.
Unique local address (ULA): It uses the network prefix FC00::/7 and is equivalent to a private IPv4 address.
Link-local address (LLA): It uses the network prefix FE80::/10 and is valid only for the local link.
Anycast address
Multicast address
Notes: Global unicast address (GUA): It is also known as an aggregatable GUA. This type of address is globally unique and is used by hosts that need to access the Internet. It is equivalent to a public IPv4 address.
Unique local address (ULA): It is a private IPv6 address that can be used only on an intranet. This type of address cannot be routed on an IPv6 public network and therefore cannot be used to directly access a public network.
Link-local address (LLA): It is another type of IPv6 address with a limited application scope.

## Slide 11: IPv6 Basics: Service Process of IPv6 Unicast Addresses
Before sending an IPv6 packet, an interface undergoes address configuration, duplicate address detection (DAD), and address resolution. The Neighbor Discovery Protocol (NDP) plays a significant role in this process.
Manually configured
Generated by the system
Dynamically generated based on the EUI-64 standard
LLA
GUA
Manually configured
Stateful address autoconfiguration
Stateless address autoconfiguration
DAD
Address resolution
Address configuration
IPv6
data forwarding
Similar to ARP requests in IPv4, ICMPv6 packets are used to generate the mappings between IPv6 addresses and data link layer addresses (usually MAC addresses).
DAD is similar to gratuitous ARP in IPv4 and is used to detect whether the current address conflicts with an address of another interface.
GUAs and LLAs are the most common IPv6 unicast addresses of interfaces. An interface can have multiple IPv6 addresses configured.

## Slide 12: IPv6 Basics: Configuration Methods of GUAs
Similar to IPv4 address assignment, IPv6 address assignment can be classified into manual configuration, stateful address autoconfiguration, and stateless address autoconfiguration.
Manual configuration
An IPv6 GUA can be:
Generated in EUI-64 format: An IPv6 GUA in EUI-64 format contains a manually configured prefix and an interface ID that is automatically generated by an interface.
Configured manually.
Stateful address autoconfiguration (DHCPv6)
Implemented through DHCPv6:
Stateless address autoconfiguration (SLAAC)
Implemented through NDP:
1
Generate an LLA.
2
Perform DAD on the LLA.
3
Send RS messages to attempt to discover routers.
4
Respond with an RA message carrying the IPv6 address prefix.
5
Generate an IPv6 unicast address.
6
Perform DAD on the IPv6 unicast address.
R1
1
Solicit
Request an IPv6 address/prefix.
DHCPv6 server
2
Advertise
Notify the client of the IPv6 address/prefix that can be assigned.
Request
Accept the IPv6 address/prefix.
Reply
Assign the IPv6 address/prefix to the client.
3
4
R2
R1

## Slide 13: IPv6 Address Application
There are two types of IPv6 address space: Provider-Aggregatable (PA) address space and Provider-Independent (PI) address space.
PA address space
The PA address space is a block of IP addresses assigned by a regional Internet registry to an Internet service provider (ISP).
An ISP can assign addresses in an address block based on user requirements. PA addresses are provided to users together with services such as private line and Internet egress. This mode is cost-effective and applies to small and midsize enterprises. However, the assigned addresses are changed if a different ISP is used.
PI address space
The PI address space is a block of IP addresses assigned by a regional Internet registry directly to end users. Users who obtain such addresses must contact an ISP to obtain the Internet access service and advertise the routes destined for related address segments on the Internet.
PI addresses allow users to connect to multiple ISPs and plan addresses flexibly. However, the cost is high. This mode applies to medium- and large-sized enterprises.
IANA
Regional Internet registry
ISP1
Users
ISP2
IPv6
address block 1
IPv6
address block 2
IANA
Regional Internet registry
ISP1
Users
ISP2
IPv6 address block

## Slide 14: IPv6 Address Planning
Step 1
Step 2
Step 3
Step 4
Requirements analysis and confirmation
IPv6 address planning scope
Address structure design
It is recommended that IPv6 addresses be planned globally and uniformly for the entire network.
Determine the basic structure of IPv6 addresses.
Design the IPv6 address structure, including the fixed prefix, user-defined prefix, and host address.
Prefix definition
Collect enterprise information related to address assignment and define prefix information.
Location and quantity
Country, region, province, city, county, campus building, floor, etc.
Physical and logical locations, such as network plane A, network plane B, and xx dedicated network.
Services, applications, and systems connected in each location
Office, R&D, sales, administration, finance, etc.
Prefix assignment and definition in a top-to-down manner
Address assignment
After the headquarters defines and plans addresses, the addresses are assigned to subordinate units as required. The subordinate units can plan the reserved subnet space.
32 bits
32 bits
64 bits
Fixed prefix
User-defined prefix
Host address
Notes: General rules for IPv6 address planning:
  Hierarchical design: The large address space of IPv6 imposes higher requirements on route summarization. Specifically, network address fragments need to be reduced and route summarization needs to be enhanced to improve routing efficiency. The hierarchical design helps reduce the size of routing tables, ease IP address expansion and configuration, and facilitate fault locating, management, and capacity planning. In the hierarchical design, an IPv6 address is divided into several independent fields. Each field can be planned individually to implement route summarization. For example, a user-defined prefix can be divided into multiple fields, with each field representing a different meaning.
  Semantics: Different fields are defined and assigned with meanings such as service type and physical location, facilitating O&M and fault locating.
  Security: Services with shared attributes have the same security requirements. Mutual access between services needs to be controlled. Services with shared attributes are assigned addresses in the same address space, facilitating security design and policy management.
  Continuity: It is recommended that IPv6 addresses in or between address segments be contiguous. This avoids wasting addresses and facilitates address management and summarization. This also eases route summarization, reduces the size of routing tables, and improves routing efficiency.
  Extensibility: Some IP addresses should be reserved for future network expansion.

## Slide 15: Example of IPv6 Address Planning
Overall IPv6 address planning of XX Bank:
32
8
4
4
4
12
Interface ID
Network prefix
Level-2 organization
Network zone
Organization
Application category
Reserved address block
In this example, the IPv6 prefix assigned to the bank is XXXX:XXXX::/32.
Field | Level-2 Organization
0000 | HQ
0001 | Branch A
0010 | 
0011 | 
... | ...
Field | Application Category
0000 | Production
0001 | Office
0010 | Development and test
0011 | Out-of-band management of network devices
0100 | Network device interconnection
0101 | Video surveillance
... | ...
Application Category | Field | Network Zone
Production | 0000 | Production terminal
 | 0001 | External DMZ
 | 0010 | E-banking web zone
 | 0011 | E-banking app zone
 | 0100 | Production service area
 | 0101 | Management service zone
 | 0110 | Core service zone
 | ... | ...
HQ - production - production service zone:
XXXX:XXXX:0000:4000::/64
HQ - production - core service zone:
XXXX:XXXX:0000:6000::/64

## Slide 16
IPv6 Basics
IPv6 Transition Technologies

## Slide 17: Introduction to IPv6 Transition Technologies
Currently, different regions in the world have different requirements for IPv6 deployment, and IPv4 networks are still the mainstream. Therefore, IPv6 and IPv4 will coexist in a certain period of time. The dual-stack, tunneling, and translation technologies can be used to implement interworking between IPv4 and IPv6 services.
IPv4/IPv6 dual stack
Tunneling technologies
Translation technologies
Devices support IPv4/IPv6. IPv4 and IPv6 are independently deployed and coexist for a period of time. This technology has little impact on existing IPv4 services.
The evolution solution is simple and easy to understand. The workload of network planning and design is relatively low.
IPv6 over IPv4 tunneling:
IPv6 packets are encapsulated with IPv4 headers and are transmitted over IPv4 tunnels. This technology connects isolated IPv6 networks through an IPv4 network.
Including manual tunnels, automatic tunnels, 6PE, and 6VPE.
IPv4 over IPv6 tunneling:
IPv4 packets are encapsulated with IPv6 headers and are transmitted over IPv6 tunnels. This technology connects isolated IPv4 networks through an IPv6 network.
Including manual tunnels, IPv6 VXLAN tunnels, and SRv6 tunnels.
IPv4 traffic is translated into IPv6 traffic (mainly IP header modification), or IPv6 traffic is translated into IPv4 traffic. This technology implements communication between native IPv4 and IPv6 networks.
A network address translation (NAT) or domain name system (DNS) device must be deployed on a network.
Translation technologies include NAT64 and IVI.
IPv6 host
IPv4 host
IPv6
Dual-stack device
Dual-stack device
IPv4
IPv6
IPv6
IPv4
Tunnel
IPv6
IPv4
NAT64/IVI gateway
DNS
IPv6 data
IPv4 data
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
IPv4
IPv4
IPv6
Tunnel
Notes: IPv4 address exhaustion fuels the urgency to transition to IPv6, but this requires existing IPv4 devices to be replaced as these devices are incompatible with IPv6 networks. The main issue is that replacing a large number of IPv4 devices will incur huge costs and interrupt services on the live networks. Therefore, the transition from IPv4 to IPv6 must be a gradual process. During the early stage of IPv4-to-IPv6 transition, IPv6 networks are scattered across a large number of IPv4 networks. Therefore, IPv6 transition technologies are required to implement IPv6 service interworking.
Note: The VXLAN and SRv6 technologies will be described in detail in subsequent courses.

## Slide 18: Tunneling Technology: IPv6 over IPv4
IPv6
IPv6 over IPv4 tunneling enables interconnection between isolated IPv6 networks over an IPv4 network.
Fundamentals of IPv6 over IPv4 tunneling:
IPv6
IPv4
IPv6 over IPv4 tunnel
IPv6 host
IPv6 host
IPv6 Header
IPv6 Data
IPv4 Header
IPv4/IPv6 dual stack is enabled on border devices (R1 and R2), and an IPv6 over IPv4 tunnel is configured.
When receiving an IPv6 packet from the connected IPv6 network, R1 encapsulates it into an IPv4 packet by attaching an IPv4 header to the IPv6 packet. This is done only if the IPv6 packet is not destined for R1 and has a tunnel interface as the next hop.
R1 transmits the resulting IPv4 packet to R2 over the IPv4 network.
R2 decapsulates the IPv4 packet by removing the IPv4 header, and sends the resulting IPv6 packet to the destination IPv6 network.
IPv6 Header
IPv6 Data
R1
(dual-stack)
Classification of IPv6 over IPv4 tunnels:
  For an IPv6 over IPv4 tunnel, the source IPv4 address must be manually specified, and the destination IPv4 address can be manually or automatically determined. From this perspective, IPv6 over IPv4 tunnels are classified into manual tunnels and automatic tunnels.
IPv6 Header
IPv6 Data
Source IPv4: source IPv4 address of the tunnel
Destination IPv4: destination IPv4 address of the tunnel
Source IPv4 address of the tunnel
Loopback 0
Next hop: IPv6 address of the peer interface Tunnel 1
Tunnel 1
Tunnel 1
Destination IPv4 address of the tunnel
Loopback 0
R2
(dual-stack)
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 19: Manual Tunnel
For a manual tunnel, the destination IPv4 address must be manually specified, as border devices cannot automatically obtain this address.
Manual IPv6 over IPv4 tunnel
A manual tunnel provides a point-to-point connection, and its source and destination addresses need to be manually specified. In a manual tunnel, an IPv6 packet is encapsulated into an IPv4 packet, with itself as the payload of the IPv4 packet.
A manual tunnel is created between two border routers to connect IPv6 networks that are isolated by IPv4 networks, or created between a border router and a host to enable the host to access an IPv6 network.
IPv6 over IPv4 GRE tunnel
An IPv6 over IPv4 GRE tunnel uses the standard GRE tunneling technology to provide a point-to-point connection. Addresses need to be specified for both ends of the tunnel.
IPv6
IPv4
Border device
(dual-stack)
Border device
(dual-stack)
IPv6 over IPv4 tunnel
IPv6
IPv4 Header
IPv6 Header
IPv6 Data
IPv6
IPv4
Border device
(dual-stack)
Border device
(dual-stack)
GRE tunnel
IPv6
IPv4 Header
IPv6 Header
IPv6 Data
GRE Header
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Manual IPv6 over IPv4 tunnel:
  Devices at both ends of a tunnel must support the IPv4/IPv6 dual stack. Other devices only need to support a single protocol stack.
  The source and destination addresses of a manual tunnel are manually configured on devices. If a border device needs to establish tunnels with several devices, manually configuring multiple tunnels on the device is complex. Therefore, manual tunnels apply when two border routers connect only two IPv6 networks.
  Tunnel forwarding mechanism: When receiving a packet from an IPv6 network, a border device searches its routing table for an entry matching the destination address of the IPv6 packet. If the outbound interface is a virtual tunnel interface, the border device encapsulates the IPv6 packet into an IPv4 packet based on the source and destination IPv4 addresses configured on the interface. The resulting IPv4 packet is then forwarded to the remote end of the tunnel over an IPv4 network. When receiving this IPv4 packet, the remote end decapsulates the packet to obtain the original IPv6 packet and processes it using the IPv6 protocol stack.
IPv6 over IPv4 GRE tunnel:
  Tunnel forwarding mechanism: Same as that of the manual IPv6 over IPv4 tunnel.

## Slide 20: Automatic Tunnel
For an automatic tunnel, you only need to configure the source IPv4 address of the tunnel, and the destination IPv4 address of the tunnel is automatically generated by the device. To automatically generate a destination IPv4 address, a tunnel interface on the device uses a special IPv6 address that contains an IPv4 address. The device obtains an IPv4 address from the destination IPv6 address of an IPv6 packet, and uses this IPv4 address as the destination address of the tunnel.
Automatic IPv4-compatible IPv6 tunnel
The destination address (special IPv6 address used by the automatic tunnel) of an IPv6 packet is an IPv4-compatible IPv6 address. The first 96 bits of the address are all 0s, and the last 32 bits are an IPv4 address.
6to4 tunnel
A 6to4 tunnel uses special IPv6 addresses that contain IPv4 addresses as the network prefix.
6to4 address format:
ISATAP tunnel
An Intra-Site Automatic Tunnel Addressing Protocol (ISATAP) tunnel uses special IPv6 addresses that contain IPv4 addresses as the interface ID.
ISATAP interface ID format:
IPv6
IPv6
IPv4-compatible IPv6 tunnel
R1
Tunnel 1
::A01:101/96
Tunnel 1
::A01:102/96
R2
IPv4 Header
IPv6 Header
IPv6 Data
Source IPv4: 10.1.1.1
Destination IPv4: 10.1.1.2
Source IPv6: ::A01:101
Destination IPv6: ::A01:102
TLA
IPv4 Address
3 bits
32 bits
FP
SLA ID
Interface ID
64 bits
13 bits
16 bits
6to4
6to4
IPv4
6to4 tunnel
6to4 router
10.1.1.1/24
10.1.1.2/24
Tunnel 1
2002:A01:101::1/48
Tunnel 1
2002:A01:102::1/48
6to4 router
IPv4
10.1.1.1/24
10.1.1.2/24
IPv4 Address
32 bits
000000ug00000000
0101111011111110
16 bits
16 bits
IPv6
IPv4
ISATAP tunnel
ISATAP router
GE0/0/1:10.1.1.1/24
Tunnel 1
LLA: FE80::5EFE:A01:101
GUA: 1::5EFE:A01:101
Host 1
3::8
Host 2
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: The data forwarding process of an automatic IPv4-compatible IPv6 tunnel is as follows:
  When receiving an IPv6 packet, R1 searches for an IPv6 route destined for ::A01:102 and finds that the next hop of the route is a virtual tunnel interface.
  R1 encapsulates the IPv6 packet into an IPv4 packet. The source address of the IPv4 packet is the source IPv4 address 10.1.1.1 of the tunnel, and the destination IPv4 address is the last 32 bits (10.1.1.2) of the IPv4-compatible IPv6 address ::A01:102.
  R1 sends the resulting IPv4 packet out from its tunnel interface. Then, the packet is routed to the destination node R2 at 10.1.1.2 over the IPv4 network. When receiving this packet, R2 decapsulates the packet to obtain the original IPv6 packet, and processes the IPv6 packet using the IPv6 protocol stack.
  The response packet returned by R2 is processed in a similar way as the IPv6 packet sent by R1.
6to4 tunnel:
  The network prefix of a 6to4 address is 64 bits long.
    The first 48 bits (2002: a.b.c.d) are determined by the IPv4 address assigned to a router and cannot be changed.
    The last 16 digits (SLA) are defined by users.

## Slide 21
Notes:   Fields in a 6to4 address:
    FP: indicates the format prefix of aggregatable GUAs. The value is 001.
    TLA: indicates the top level aggregator. The value is 0x0002.
    SLA: indicates the site level aggregator.
ISATAP tunnel:
  First 64 bits of an ISATAP address: The device at one end of a tunnel obtains the first 64 bits by sending a request to the ISATAP router through NDP, and automatically generates an ISATAP IPv6 address accordingly.
  ISATAP interface ID:
    When the IPv4 address is globally unique, the "u" bit is set to 1; otherwise, the "u" bit is set to 0. ISATAP tunnels are typically applied within sites. Therefore, the IPv4 addresses in interface IDs do not need to be globally unique.
    The "g" bit is an IEEE group/individual bit and its value is fixed at 0.
  As shown in the figure, Host 2 on the IPv4 network supports the IPv4/IPv6 dual stack and has a private IPv4 address (10.1.1.2/24). You can perform the following operations on Host 2 to enable the ISATAP function:
    Configure an ISATAP tunnel interface. Then, Host 2 generates an ISATAP interface ID based on its IPv4 address, and generates an ISATAP link-local IPv6 address (FE80::5EFE:A01:102) based on the interface ID, so that it can access the IPv6 network on the local link.
    Configure Host 2 to automatically obtain an IPv6 GUA (1::5EFE:A01:102). When Host 2 communicates with another IPv6 host, it uses the IPv4 address in the next-hop IPv6 address as the destination address in an IPv4 header, and sends the packet out through its tunnel interface.

## Slide 22: Tunneling Technology: 6PE
To provide IPv6 services for users, carriers do not need to build new IPv6 backbone networks; instead, they can use existing IPv4 networks to connect isolated IPv6 sites. IPv6 Provider Edge (6PE) is designed based on this concept.
The 6PE solution connects isolated IPv6 networks using multiprotocol label switching (MPLS) tunnels over IPv4 networks. 6PE implements IPv4/IPv6 dual stack on provider edges (PEs) of Internet service providers (ISPs), and uses the Multiprotocol Extensions for Border Gateway Protocol (MP-BGP) to assign labels to IPv6 routes. In this way, isolated IPv6 networks are connected through IPv4 tunnels between PEs.
IPv4
IPv4 tunnel (MPLS)
Dual-stack
6PE1
CE2
CE1
IPv6 link
IPv6 link
Dual-stack
6PE2
CEs and PEs use IPv6 routing protocols such as IGP, EBGP, and static routing to exchange IPv6 routes.
PEs use IPv4 routing protocols to exchange IPv4 routes with P devices and other PEs.
Tunnels are established between PEs to transparently transmit IPv6 packets.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Advantages of 6PE:
  Easy maintenance: All configurations are performed on PEs. IPv6 services are carried over the existing IPv4 networks, simplifying network maintenance. Additionally, users on IPv6 networks are unaware of the IPv4 networks.
  Low network construction costs: Carriers can provide IPv6 services to users over existing MPLS networks without upgrading the networks. 6PE devices can also provide various types of services, such as IPv6 VPN and IPv4 VPN.

## Slide 23: Intra-AS 6PE
Isolated IPv6 networks can connect to the same autonomous system (AS). PEs in the AS exchange IPv6 routes by establishing MP-IBGP peer relationships.
The following figure shows how CE2 sends a route to CE1 and how CE1 sends a packet to CE2 in an intra-AS 6PE scenario.
  I-L is the inner label (MP-IBGP label), which is assigned by MP-BGP. It indicates the outbound interface or CE to which the packet should be forwarded.
  O-L is the outer tunnel label (MPLS Label), which is assigned by MPLS. It directs the packet to the BGP next hop.
6PE1
CE1
IPv6 EBGP
6PE2
CE2
IPv6 EBGP
IPv4 IBGP
MPLS LSP
CE2
6PE2
6PE1
CE1
Data
Data
I-L1
O-L1
Data
Data
1::1/128
1::1/128
1::1/128 I-L1
Next hop: 6PE2
1::1/128
Push
Pop
IPv6 data
IPv4 data
Route
IPv6 EBGP
IPv6 EBGP
IPv4 IBGP
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: The route transmission process in an intra-AS 6PE scenario is as follows:
  CE2 sends an intra-AS IPv6 route to its EBGP peer 6PE2.
  Upon receipt, 6PE2 changes the next hop of the IPv6 route to itself, and assigns an inner label to the IPv6 route. Then, 6PE2 sends the labeled IPv6 route to its IBGP peer 6PE1.
  When receiving the labeled IPv6 route, 6PE1 recurses the route to a tunnel, and adds the route to the local forwarding table. Then, 6PE1 changes the next hop of the IPv6 route to itself, removes the label from the route, and sends the route to its EBGP peer CE1.
The packet transmission process in an intra-AS 6PE scenario is as follows:
  CE1 sends an ordinary IPv6 packet to 6PE1 over an IPv6 link on the public network.
  Upon receipt of the IPv6 packet, 6PE1 looks up the destination address of the packet in its forwarding table, and encapsulates the packet with inner and outer labels. Then, 6PE1 sends the resulting IPv6 packet to 6PE2 over a public network tunnel.
  When receiving the IPv6 packet, 6PE2 removes the inner and outer labels and forwards the resulting IPv6 packet to CE2 based on the destination address over an IPv6 link.

## Slide 24: Explicit Null Label Shared by 6PE Routes
In a 6PE networking, by default, each 6PE route to be sent to 6PE peers is assigned a label. This will cause a large number of label resources to be consumed if many 6PE routes need to be sent.
After 6PE routes are configured to share the same explicit null label, all 6PE routes to be sent to 6PE peers share the explicit null label 2. The number of required labels is irrelevant to the number of 6PE routes to be sent. This greatly saves label resources on 6PE devices.
Explicit null label 2 is a special label that must be popped out on the egress PE, and packets must be forwarded based on IPv6.
CE2
6PE2
6PE1
CE1
Data
Data
2
O-L1
Data
Data
1::1/128
1::1/128
1::1/128 I-L1
Next hop: PE2
1::1/128
Push
Pop
IPv6 EBGP
IPv6 EBGP
IPv4 IBGP
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: When 6PE routes are configured to share the same explicit null label on 6PE2, 6PE2 advertises 6PE routes with an explicit null label to 6PE1 without applying for labels for the routes.
When forwarding data to 6PE2, 6PE1 adds two labels to the data. The outer label is distributed by LDP pointing to 6PE2, and the inner label is an explicit null label distributed by MP-BGP.
When the IPv6 data packet arrives at 6PE2, 6PE2 pops out the explicit null label and forwards the packet to CE2.

## Slide 25: Tunneling Technology: 6VPE
All IPv6 services connected through 6PE run in the same VPN and cannot be logically isolated. Therefore, 6PE can be used only for open and unprotected IPv6 network interconnection. To isolate the connected IPv6 services logically, that is, to implement IPv6 VPNs, use the IPv6 VPN Provider Edge (6VPE) technology.
6VPE is an extension of BGP/MPLS IPv6 VPN. It transmits IPv6 VPN services over an IPv4 MPLS backbone network.
IPv4 MPLS
BGP/MPLS IPv6 VPN
Dual-stack
6VPE1
Dual-stack
6VPE2
A BGP/MPLS IPv6 VPN tunnel is established between PEs to transmit IPv6 VPN routes.
VPN2
Site
VPN1
Site
CE (IPv6)
CE (IPv6)
VPN2
Site
VPN1
Site
CE (IPv6)
CE (IPv6)
CEs and PEs use IPv6 routing protocols such as IGP, EBGP, and static routing to exchange IPv6 routes.
6VPE uses MP-BGP to advertise VPNv6 routes on an IPv4 MPLS backbone network, uses MPLS to assign labels to identify IPv6 packets, and uses tunneling mechanisms such as LSP and MPLS TE to transmit private network data on the backbone network.
If the backbone network is an IPv4 network, IPv4 addresses are used to establish VPNv6 peer relationships between PEs to transmit IPv6 VPN routes. For these routes, IPv4 tunnels on the backbone network can be selected to transmit IPv6 VPN services.
Except the routing protocols running between PEs and CEs, implementation of 6VPE is the same as that of IPv4 VPN.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: In 6VPE, IPv6 routing protocols run between PEs and CEs. The following IPv6 routing protocols can be used to provide IPv6 VPN services:
  BGP4+
  Static IPv6 routing
  OSPFv3
  IS-IS for IPv6

## Slide 26: Configuring 6VPE (1)
[HUAWEI] ip vpn-instance vpn-instance-name
Configure a VPN instance.
A route distinguisher (RD) and VPN target extended community are configured for the VPN instance IPv6 address family.
[HUAWEI-vpn-instance-vpna] ipv6-family
[HUAWEI-vpn-instance-vpna-af-ipv6] route-distinguisher route-distinguisher
[HUAWEI-vpn-instance-vpna-af-ipv6] vpn-target vpn-target [ both | export-extcommunity | import-extcommunity ]
Bind the VPN instance to an interface.
[HUAWEI-GigabitEthernet0/0/1] ip binding vpn-instance vpn-instance-name
[HUAWEI-GigabitEthernet0/0/1] ipv6 enable
[HUAWEI-GigabitEthernet0/0/1] ipv6 address { ipv6-address prefix-length | ipv6-address/prefix-length }
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Note: This course uses a Huawei NetEngine 8000 series router as an example to describe how to configure 6VPE.
Command: <HUAWEI>system-view [ immediately ]
  immediately: indicates that the configuration takes effect immediately.

## Slide 27: Configuring 6VPE (2)
Configure MP-IBGP between PEs to transmit VPNv6 routes.
[HUAWEI] bgp as-number
[HUAWEI-bgp] peer ipv4-address as-number as-number
[HUAWEI-bgp] peer ipv4-address connect-interface interface-number
The BGP VPNv6 address family view is enabled and displayed, and the ability to exchange VPNv6 routes with peers is enabled in this view.
[HUAWEI-bgp] ipv6-family vpnv6
[HUAWEI-bgp-af-ipv6] peer ipv4-address enable
The remote PE is configured as an IBGP peer in the BGP view.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 28: Configuring 6VPE (3)
Configure route exchange between PEs and CEs. (A static route is used as an example. The configuration on CEs is the same as that of an ordinary IPv6 static route, and is not mentioned here.)
[PE] ipv6 route-static vpn-instance vpn-instance-name dest-ipv6-address prefix-length { interface-type interface-number [ nexthop-ipv6-address ] | vpn-instance vpn-destination-name nexthop-ipv6-address | nexthop-ipv6-address } [ preference preference ]
An IPv6 static route is configured for the VPN instance enabled with the IPv6 address family.
[PE-bgp] ipv6-family vpn-instance vpn-instance-name
[PE-bgp-bgp6-vpnb] import-route static [ med med | route-policy route-policy-name ]
The BGP-VPN instance IPv6 address family view is displayed, and the configured static route is imported to the routing table of the BGP-VPN instance IPv6 address family.
med med: specifies the MED of the imported route. The value is an integer in the range from 0 to 4294967295.
route-policy route-policy-name: specifies a route-policy for filtering routes and modifying route attributes when routes of other routing protocols are imported.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Note: For details about route exchange between PEs and CEs, see the corresponding product documentation.

## Slide 29: Example of Configuring 6VPE (1)
Configuration requirements:
  Users at different sites desire IPv6 data communication between each other across a public network without having the internal route information known to the public network, and also implement service isolation.
  As shown in the figure, CE1 and CE2 belong to vpna. It is required that 6VPE be configured to allow sites in vpna to communicate with each other through an MPLS backbone network, and PEs and CEs exchange static routes.
GE0/0/2
10.0.0.1/30
GE0/0/2
10.0.0.2/30
Loopback 0
3.3.3.3/32
Loopback 0
2.2.2.2/32
GE0/0/1
2001:DB8:1::2/64
GE0/0/1
2001:DB8:2::2/64
GE0/0/1
2001:DB8:1::1/64
GE0/0/1
2001:DB8:2::1/64
Loopback 1
2001:DB8:5::5/128
Loopback 1
2001:DB8:6::6/128
AS 200
AS 100
AS 300
CE1
vpna
PE1
PE2
Configure IPv4 and IPv6 addresses for interfaces. (The configuration details are not provided here.)
[PE1] mpls lsr-id 2.2.2.2
[PE1] mpls
[PE1-mpls] quit
[PE1] mpls ldp
[PE1-mpls-ldp] quit
[PE1] interface GigabitEthernet0/0/2
[PE1-GigabitEthernet2/0/0] mpls
[PE1-GigabitEthernet2/0/0] mpls ldp
Enable MPLS and MPLS LDP on the backbone network, and enable PEs to establish an LDP LSP.
Configure IS-IS on PE1 and PE2 so that they can learn routes to each other's interface (loopback 0). (The configuration details are not provided here.)
The configuration on PE2 is similar to that on PE1, and is not provided here.
CE2
vpna
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 30: Example of Configuring 6VPE (2)
Configuration requirements:
  Users at different sites desire IPv6 data communication between each other across a public network without having the internal route information known to the public network, and also implement service isolation.
  As shown in the figure, CE1 and CE2 belong to vpna. It is required that 6VPE be configured to allow sites in vpna to communicate with each other through an MPLS backbone network, and PEs and CEs exchange static routes.
GE0/0/2
10.0.0.1/30
GE0/0/2
10.0.0.2/30
Loopback 0
3.3.3.3/32
Loopback 0
2.2.2.2/32
GE0/0/1
2001:DB8:1::2/64
GE0/0/1
2001:DB8:2::2/64
GE0/0/1
2001:DB8:1::1/64
GE0/0/1
2001:DB8:2::1/64
Loopback 1
2001:DB8:5::5/128
Loopback 1
2001:DB8:6::6/128
AS 200
AS 100
AS 300
CE1
vpna
PE1
PE2
CE2
vpna
Create a VPN instance supporting the IPv6 address family on each PE, and bind the VPN instance to the PE's interface connected to a CE.
[PE1] ip vpn-instance vpna
[PE1-vpn-instance-vpna] ipv6-family
[PE1-vpn-instance-vpna-af-ipv6] route-distinguisher 100:1
[PE1-vpn-instance-vpna-af-ipv6] vpn-target 22:22 both
[PE1] interface GigabitEthernet0/0/1
[PE1-GigabitEthernet0/0/1] ip binding vpn-instance vpna
[PE1-GigabitEthernet0/0/1] ipv6 enable
[PE1-GigabitEthernet0/0/1] ipv6 address 2001:DB8:1::2 64
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
The configuration on PE2 is similar to that on PE1, and is not provided here.

## Slide 31: Example of Configuring 6VPE (3)
Configuration requirements:
  Users at different sites desire IPv6 data communication between each other across a public network without having the internal route information known to the public network, and also implement service isolation.
  As shown in the figure, CE1 and CE2 belong to vpna. It is required that 6VPE be configured to allow sites in vpna to communicate with each other through an MPLS backbone network, and PEs and CEs exchange static routes.
GE0/0/2
10.0.0.1/30
GE0/0/2
10.0.0.2/30
Loopback 0
3.3.3.3/32
Loopback 0
2.2.2.2/32
GE0/0/1
2001:DB8:1::2/64
GE0/0/1
2001:DB8:2::2/64
GE0/0/1
2001:DB8:1::1/64
GE0/0/1
2001:DB8:2::1/64
Loopback 1
2001:DB8:5::5/128
Loopback 1
2001:DB8:6::6/128
AS 200
AS 100
AS 300
CE1
vpna
PE1
PE2
CE2
vpna
Enable PEs to establish a VPNv6 peer relationship.
[PE1] bgp 200
[PE1-bgp] peer 3.3.3.3 as-number 200
[PE1-bgp] peer 3.3.3.3 connect-interface loopback 0
[PE1-bgp] ipv6-family vpnv6
[PE1-bgp-af-vpnv6] peer 3.3.3.3 enable
[PE2] bgp 200
[PE2-bgp] peer 2.2.2.2 as-number 200
[PE2-bgp] peer 2.2.2.2 connect-interface loopback 0
[PE2-bgp] ipv6-family vpnv6
[PE2-bgp-af-vpnv6] peer 2.2.2.2 enable
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 32: Example of Configuring 6VPE (4)
Configuration requirements:
  Users at different sites desire IPv6 data communication between each other across a public network without having the internal route information known to the public network, and also implement service isolation.
  As shown in the figure, CE1 and CE2 belong to vpna. It is required that 6VPE be configured to allow sites in vpna to communicate with each other through an MPLS backbone network, and PEs and CEs exchange static routes.
GE0/0/2
10.0.0.1/30
GE0/0/2
10.0.0.2/30
Loopback 0
3.3.3.3/32
Loopback 0
2.2.2.2/32
GE0/0/1
2001:DB8:1::2/64
GE0/0/1
2001:DB8:2::2/64
GE0/0/1
2001:DB8:1::1/64
GE0/0/1
2001:DB8:2::1/64
Loopback 1
2001:DB8:5::5/128
Loopback 1
2001:DB8:6::6/128
AS 200
AS 100
AS 300
CE1
vpna
PE1
PE2
CE2
vpna
Configure static routes on PEs and CEs, and import the static routes to the routing table of the BGP-VPN instance IPv6 address family on each PE.
[PE1] ipv6 route-static vpn-instance vpna 2001:DB8:5:: 64 2001:DB8:1::1
[PE1] bgp 200
[PE1-bgp] ipv6-family vpn-instance vpna
[PE1-bgp6-vpna] import-route static
[CE1] ipv6 route-static :: 0 2001:DB8:1::2
[PE2] ipv6 route-static vpn-instance vpna 2001:DB8:6:: 64 2001:DB8:2::1
[PE2] bgp 200
[PE2-bgp] ipv6-family vpn-instance vpna
[PE2-bgp6-vpna] import-route static
[CE2] ipv6 route-static :: 0 2001:DB8:2::2
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 33: Verifying the Configuration
On PEs, check whether a VPNv6 peer relationship is established.
[PE1]display bgp vpnv6 all peer
BGP local router ID : 10.0.0.1
Local AS number : 200
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
3.3.3.3 4 200 19 19 0 00:12:25 Established 1
Check whether CE1 can ping the loopback 1 interface of CE2.
[CE1]ping ipv6 -a 2001:db8:5::5 2001:db8:6::6
PING 2001:db8:6::6 : 56 data bytes, press CTRL_C to break
Request time out
Reply from 2001:DB8:6::6
bytes=56 Sequence=2 hop limit=62 time = 50 ms
Reply from 2001:DB8:6::6
bytes=56 Sequence=3 hop limit=62 time = 40 ms
Reply from 2001:DB8:6::6
bytes=56 Sequence=4 hop limit=62 time = 30 ms
Reply from 2001:DB8:6::6
bytes=56 Sequence=5 hop limit=62 time = 30 ms
--- 2001:db8:6::6 ping statistics ---
5 packet(s) transmitted
4 packet(s) received
20.00% packet loss
round-trip min/avg/max = 30/37/50 ms
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 34: Tunneling Technology: IPv4 over IPv6
In the late stage of IPv4-to-IPv6 transition, IPv6 networks have been widely deployed, and IPv4 networks are siloed sites scattered among IPv6 networks. Connecting these isolated IPv4 networks using private lines is costly, so a general practice is to leverage tunneling technology, just as IPv4 over IPv6 tunneling does.
With IPv4 over IPv6 tunneling, tunnels can be created on IPv6 public networks to enable communication between isolated IPv4 networks.
IPv4
IPv4
IPv6
IPv4 over IPv6 tunnel
IPv4 host 2
IPv4 host 1
IPv4 Header
IPv4 Data
IPv6 Header
IPv4 Header
IPv4 Data
IPv4 Header
IPv4 Data
R1
(dual-stack)
R2
(dual-stack)
An IPv4 over IPv6 tunnel is manually configured between border routers connecting two IPv4 networks to an IPv6 network, with the source addresses or interfaces and the destination addresses statically specified.
In the figure, packets passing through the IPv4 over IPv6 tunnel are processed on border nodes R1 and R2, and all the other nodes (Host 1, Host 2, and nodes between R1 and R2) are unaware of the tunnel. IPv4 packets are transmitted between Host 1 and R1 and between R2 and Host 2, and IPv6 packets are transmitted between R1 and R2. Therefore, R1 and R2 must be able to process both IPv4 and IPv6 packets; that is, IPv4/IPv6 dual stack must be enabled on both R1 and R2.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Packet processing on an IPv4 over IPv6 tunnel:
  IPv4 packet forwarding: Host 1 sends an IPv4 packet destined for Host 2 to R1.
  Tunnel encapsulation: When receiving the IPv4 packet from Host 1, R1 discovers that the destination address of the IPv4 packet is not its own and the next hop is a tunnel interface, so R1 attaches an IPv6 header to the IPv4 packet. Specifically, in the IPv6 header, R1 encapsulates both its own and R2's IPv6 addresses into the Source Address and Destination Address fields, respectively, sets the Version field to 6 and the Next Header field to 4, and encapsulates the fields that ensure effective transmission of the packet along the tunnel based on the configuration.
  Tunnel forwarding: R1 searches its IPv6 routing table for an entry matching the destination address in the IPv6 header, and forwards the IPv6 packet to R2. Other nodes on the IPv6 network are unaware of the tunnel and process the IPv6 packet as an ordinary IPv6 packet.
  Tunnel decapsulation: Upon receipt of the IPv6 packet, R2 discovers that the destination address is its own IPv6 address and the encapsulated packet is an IPv4 packet based on the Next Header field, and then decapsulates the IPv6 packet by removing the IPv6 header based on the Version field.
  IPv4 packet forwarding: R2 searches its IPv4 routing table for an entry matching the destination address of the IPv4 packet and forwards the packet to Host 2.

## Slide 35: Translation Technology: NAT64
NAT64 is a network address translation technology that translates IPv6 addresses into IPv4 addresses.
A node on an IPv4 network cannot directly communicate with a node on an IPv6 network, because the two protocol stacks are not compatible. To enable communication between them, a NAT64-capable device can be deployed to implement translation between IPv6 and IPv4.
To determine whether to perform NAT64 on a data packet, a NAT64 device checks whether the destination address of the packet contains an IPv6 prefix predefined for NAT64.
  If so, the packet is destined for an IPv4 network, and the device performs NAT64 on the packet and forwards it to the IPv4 network.
  If not, the packet is destined for an IPv6 network, and the device directly forwards the packet to the IPv6 network without performing NAT64 on the packet.
IPv6
IPv6 user
DNS64
IPv6 Internet
IPv6 server
IPv4 Internet
IPv4 server
IPv6 data
IPv4 data
NAT64
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Scenario where IPv6 users access IPv4 servers:
  At the early stage of IPv4-to-IPv6 evolution, carriers provide users with single-stack IPv6 access. However, lots of Internet servers still use IPv4 and do not support dual stack. This requires carriers to provide NAT64 devices for single-stack IPv6 users to access IPv4 servers.
  The carriers only need to assign IPv6 addresses to users, with communication between IPv6 devices implemented based on IPv6 routes. Access from IPv6 users to IPv4 services is implemented through NAT64 devices that support dual stack.
  There are two NAT64 modes: static and dynamic. Static NAT64 is recommended when a small number of IPv6 users use fixed IP addresses, while dynamic NAT64 is recommended when a large number of IPv6 users use unfixed IP addresses.
Scenario where IPv4 users access IPv6 servers:
  At the late stage of IPv4-to-IPv6 evolution, many service providers have begun to provide IPv6 services. However, there are still many single-stack IPv4 users on the Internet. To retain these users, the service providers deploy NAT64 devices, which allow these users to access IPv6 servers.
  In this scenario, service providers only need to assign IPv6 addresses to servers, without the need to upgrade access devices. NAT64 devices, which must support dual stack, are deployed at the egresses, and communication between IPv6 devices is implemented based on IPv6 routes. IPv4-to-IPv6 access is implemented using the static NAT64 technology.

## Slide 36: NAT64 Prefixes
The device determines whether to perform NAT64 on an IPv6 packet by checking whether the IPv6 packet contains a NAT64 prefix.
There are two types of NAT64 prefixes:
  Well-known prefix: 64:FF9B::/96, which exists by default and does not need to be configured.
  Predefined prefix: a prefix with the length of 32, 40, 48, 56, 64, or 96 bits.
Where an IPv4 address is embedded in an IPv6 address depends on the length of the predefined NAT64 prefix, as shown in the following figure.
  In a predefined NAT64 prefix, PL indicates the length of the prefix, suffix is a random value (the device does not process this field), and U is the reserved octet whose value must be set to 0.
Prefix (32)
32
V4 (32)
U
Suffix
Prefix (40)
40
V4 (24)
U
Suffix
Prefix (48)
48
(16)
U
Suffix
Prefix (56)
56
(8)
U
Suffix
Prefix (64)
64
U
Suffix
(8)
(16)
V4 (24)
V4 (32)
Prefix (96)
96
V4 (32)
PL
If an IPv4 address is 192.168.0.1 and the NAT prefix is 2001:DB8::/64, the IPv6 address corresponding to this IPv4 address is 2001:0DB8:0000:0000:00C0:A800:0100:0000, which can be abbreviated to 2001:DB8::C0:A800:100:0.
When you configure a DNS64 server, ensure that it has the same NAT64 prefix and prefix length as the NAT64 device.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: NAT64 types:
  PAT-based NAT64: translates both addresses and port numbers by mapping [IPv6 address, port number] into [IPv4 address, port number]. Multiple IPv6 addresses can be translated into the same IPv4 address. The mappings are differentiated by port number. This mode is commonly used.
  No-PAT–based NAT64: translates only addresses by mapping [IPv6 address] into [IPv4 address]. There are one-to-one mapping relationships between IPv6 and IPv4 addresses.

## Slide 37: Dynamic NAT64
Dynamic NAT64 applies to the scenarios where a large number of IPv6 users use unfixed IP addresses. When an IPv6 user accesses an IPv4 server, a NAT64 device dynamically translates the IPv6 address in the user packet into an IPv4 address from an address pool, converts the IPv6 packet into an IPv4 packet, and then sends the IPv4 packet to the IPv4 server.
The NAT64 device then creates a session table for the IPv6-to-IPv4 traffic and records the address mapping. The NAT64 device forwards the IPv4-to-IPv6 traffic that matches an entry in the session table to the corresponding IPv6 user based on the address mapping.
IPv6 user
DNS64
IPv4 Internet
NAT64
IPv4 server
1
2
3
DNS AAAA Request
DNS AAAA Reply
(64:FF9B::101:101)
HTTP Request
SA/Port: 2001:DB8::2/90
DA/Port: 64:FF9B::101:101/80
2001:DB8::2/64
4
HTTP Request
SA/Port: 2.1.1.10/190
DA/Port: 1.1.1.1/80
example.huawei.com
1.1.1.1
6
HTTP Reply
SA/Port: 64:FF9B::101:101/80
DA/Port: 2001:DB8::2/90
5
HTTP Reply
SA/Port: 1.1.1.1/80
DA/Port: 2.1.1.10/190
IPv4 Address Pool
2.1.1.10/24
64:FF9B::0101:0101
1.1.1.1
96 bits
32 bits
IN_SA/Port | IN_DA/Port | OUT_SA/Port | OUT_DA/Port
2001:DB8::2 /90 | 64:FF9B::101:101 /80 | 2.1.1.10 /190 | 1.1.1.1 /80
Session table on the NAT64 firewall
IPv6 data
IPv4 data
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Dynamic NAT64 mapping process:
  A single-stack IPv6 user sends an AAAA DNS request for a remote service (example.huawei.com).
  After receiving the request, the DNS64 server parses the AAAA request. If no IPv6 address is found, it sends an A request, and parses the received reply packet to obtain the service IPv4 address (1.1.1.1). The DNS64 server then combines the IPv4 address and the preconfigured NAT64 prefix 64::/n (64:FF9B::/96) into the IPv6 address 64:FF9B::101:101, and sends this IPv6 address to the user.
  When receiving the DNS64 reply from the DNS64 server, the user sends a packet with the IPv6 address as the destination address to the remote server.
  After receiving the IPv6 packet from the user, the NAT64 device extracts the IPv4 address (1.1.1.1) from the IPv6 packet using the address translation algorithm, changes the destination address of the packet to this IPv4 address, changes the source address of the packet to an IPv4 address (2.1.1.10) from the NAT address pool based on the address mapping configured in the NAT64 policy, and converts the IPv6 packet into an IPv4 packet. The NAT64 device then sends the IPv4 packet to the remote server on the IPv4 network, and generates a session table with the address mapping.
  Upon receipt of the IPv4 packet, the IPv4 server returns a reply packet.
  After receiving the reply packet from the IPv4 server, the NAT64 device converts the IPv4 packet into an IPv6 packet according to the session table, and sends the IPv6 packet to the IPv6 user.
DNS AAAA and A records:
  AAAA record: maps a host name or domain name to an IPv6 address.
  A record: maps a domain name to an IPv4 address.

## Slide 38: Static NAT64
Static NAT64 allows for static mappings between IPv6 and IPv4 addresses. These mappings will not be updated or age and will always exist unless you delete them. Both IPv6-to-IPv4 traffic and IPv4-to-IPv6 traffic can trigger the creation of session tables. In this way, not only IPv6 users can access IPv4 servers, but also IPv4 users can access IPv6 servers.
When users access services of a different protocol stack (IPv4-to-IPv6 or IPv6-to-IPv4), the device translates the destination address in packets between protocol stacks according to the corresponding static address mapping.
DNS
IPv4 Internet
NAT64
1
2
4
DNS A Request
DNS A Reply
(2.1.1.10)
HTTP Request
SA/Port: 64:FF9B::101:101/80
DA/Port: 2001:DB8::2/90
example.huawei.com
2001:DB8::2/64
3
HTTP Request
SA/Port: 1.1.1.1/80
DA/Port: 2.1.1.10/190
IPv4 user
1.1.1.1/24
5
HTTP Reply
SA/Port: 2001:DB8::2/90
DA/Port: 64:FF9B::101:101/80
6
HTTP Reply
SA/Port: 2.1.1.10/190
DA/Port: 1.1.1.1/80
OUT_DA/Port | OUT_SA/Port | IN_DA/Port | IN_SA/Port
2001:DB8::2 /90 | 64:FF9B::101:101 /80 | 2.1.1.10 /190 | 1.1.1.1 /80
Session table on the NAT64 firewall
Static mapping:
2001:DB8::2 <-----> 2.1.1.10
Prefix64:
64:FF9B::/96
The relationship between the domain name and address has been registered.
IPv6 data
IPv4 data
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Static NAT64 mapping process:
  An IPv4 user sends request A (example.huawei.com) to the DNS server.
  After receiving the request, the DNS server parses the request to obtain the IPv4 address (2.1.1.10) corresponding to the domain name, and sends a reply containing the IPv4 address to the user. In this scenario, the mapping between the domain name and IPv4 address has been predefined on the DNS server. If the DNS A request does not contain any IPv4 address, the packet is discarded.
  After receiving the DNS reply, the user sends a packet with the obtained IPv4 address as the destination address to the remote server.
  Upon receipt of the IPv4 packet, the NAT64 device translates the destination IPv4 address into an IPv6 address (2001:DB8::2) according to the preconfigured static address mapping (based on which a server mapping table is generated), combines the source IPv4 address and the preconfigured NAT64 prefix into a source IPv6 address (64:FF9B::101:101), and converts the IPv4 packet into an IPv6 packet. The NAT64 device then sends the IPv6 packet to the remote server on the IPv6 network, and generates a session table.
  Upon receipt of the IPv6 packet, the server returns a reply packet.
  After receiving the reply packet from the IPv6 server, the NAT64 device converts the IPv6 packet into an IPv4 packet according to the session table, and sends the IPv4 packet to the IPv4 user.

## Slide 39: Configuring a NAT64 Prefix
[HUAWEI] nat64 enable
Enable NAT64 globally or on an interface.
When NAT64 is enabled globally, it takes effect on all interfaces.
[HUAWEI] nat64 prefix prefix prefix-length
Configure a NAT64 prefix.
[HUAWEI-GE1/0/1] nat64 enable
prefix: specifies the prefix of an IPv6 address. The value is in the format X:X:X:X:X:X:X:X.
prefix-length: specifies the prefix length. The value can be 32, 40, 48, 56, 64, or 96.
[HUAWEI] display nat64 prefix
Check the NAT64 prefix configuration.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: NAT64 prefix configuration:
  A NAT64 prefix must be different from the IPv6 address prefix of any interface on the device. Otherwise, the device considers the packets whose destination IPv6 addresses are on the same network segment as the interfaces to be NAT64 packets, and starts NAT64 processing for these packets.
  When multiple NAT64 prefixes are configured and dynamic NAT64 is used, all of these NAT64 prefixes can be used for NAT64 translation of IPv6-to-IPv4 traffic. On the other hand, if static NAT64 is used, the device randomly selects one of these prefixes.
Note: This course uses a Huawei USG6000 series firewall as an example to describe how to configure NAT64.

## Slide 40: Configuring Dynamic NAT64
[HUAWEI] nat address-group group-name [ group-number ]
Configure a NAT address pool.
[HUAWEI-address-group-nataddr] mode { pat | full-cone { global | local } [ no-reverse ] }
[HUAWEI-address-group-nataddr] section section-id start-address [ end-address ]
IP address segments in the IP address pool are configured.
The address pool mode is configured. By default, the PAT mode is used.
[HUAWEI] nat-policy
Configure a NAT policy.
[HUAWEI-policy-nat] rule name rule-name
[HUAWEI-policy-nat-rule-abc] nat-type nat64
The NAT policy type is configured.
Other configurations are similar to the NAT configuration on a firewall and are not provided here.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: Command: mode { pat | full-cone { global | local } [ no-reverse ] }
  pat: specifies the PAT mode.
  full-cone: specifies the 3-tuple NAT mode.
  global: specifies the global 3-tuple NAT mode. The generated server mapping table does not contain security zone parameters and is not subject to restrictions of interzone relationships.
  local: specifies the local 3-tuple NAT mode. The generated server mapping table contains security zone parameters and is subject to restrictions of interzone relationships.
  no-reverse: specifies that no reverse server mapping table will be generated.

## Slide 41: Configuring Static NAT64
[HUAWEI] nat64 static ipv6-address ipv4-address [ route ]
Configure static NAT64.
[HUAWEI] nat64 static protocol icmp ipv6-address ipv4-address [ route ]
[HUAWEI] nat64 static protocol { tcp | udp } ipv6-address [ ipv6-port ] ipv4-address [ipv4-port ] [ route ]
Static NAT64 mapping for TCP or UDP is configured.
Static NAT64 mapping for ICMP is configured.
Static NAT64 mapping for a specified IPv6 address is configured.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 42: Example for Configuring Dynamic NAT64 (1)
Configuration requirements:
  Firewall 1 supports the IPv4/IPv6 dual stack and is connected to an IPv4 network and an IPv6 network.
  The IPv6 network has a large number of PCs using unfixed IP addresses. These PCs need to access the server on the IPv4 network through the domain name example.huawei.com.
DNS64
Firewall 1
IPv6 PC
2001:DB8::1/64
IPv4 server
1.1.1.2/24
IPv6 network
GE1/0/1
2001:DB8::2/64
GE1/0/2
1.1.1.1/24
Trust
Untrust
Configure IPv4 and IPv6 addresses for Firewall 1 and configure security zones. (The configuration details are not provided here.)
[FW1] interface GigabitEthernet 1/0/1
[FW1-GigabitEthernet1/0/1] nat64 enable
Enable NAT64 on GE1/0/1 of Firewall 1.
[FW1] nat64 prefix 2001:db8:1:: 96
Set the NAT64 prefix to 2001:db8:1::/96 (a predefined prefix).
[FW1] security-policy
[FW1-policy-security] rule name sec1
[FW1-policy-security-rule-sec1] source-zone untrust
[FW1-policy-security-rule-sec1] destination-zone trust
[FW1-policy-security-rule-sec1] source-address 2001:db8:: 64
[FW1-policy-security-rule-sec1] action permit
Configure a security policy.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI

## Slide 43: Example for Configuring Dynamic NAT64 (2)
Configuration requirements:
  Firewall 1 supports the IPv4/IPv6 dual stack and is connected to an IPv4 network and an IPv6 network.
  The IPv6 network has a large number of PCs using unfixed IP addresses. These PCs need to access the server on the IPv4 network through the domain name example.huawei.com.
DNS64
Firewall 1
IPv6 PC
2001:DB8::1/64
IPv4 server
1.1.1.2/24
IPv6 network
GE1/0/1
2001:DB8::2/64
GE1/0/2
1.1.1.1/24
Trust
Untrust
[FW1] nat-policy
[FW1-policy-nat] rule name nat64
[FW1-policy-nat-rule-nat64] nat-type nat64
[FW1-policy-nat-rule-nat64] source-zone untrust
[FW1-policy-nat-rule-nat64] destination-zone trust
[FW1-policy-nat-rule-nat64] source-address 2001:db8:: 64
[FW1-policy-nat-rule-nat64] action source-nat address-group pool1
Configure dynamic NAT64.
[FW1] nat address-group pool1
[FW1-address-group-pool1] mode pat
[FW1-address-group-pool1] section 1 1.1.1.6 1.1.1.10
Configure a NAT64 address pool.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: The destination address of IPv6 packets sent by the IPv6 PC is the NAT64 address 2001:DB8:1::101:102/96.
Other configurations:
  Configure the DNS64 server.
    Set the IPv6 prefix of the DNS64 server to 2001:DB8:1::/96, which is the NAT64 prefix of Firewall 1.
    Configure reachable routes from the DNS64 server to the PC and server.
  Configure the IPv6 address, route, and DNS server for the PC. (The method of configuring an IPv6 address and a route for the PC varies according to the PC operating system. The detailed configuration procedure is not provided here.)
    Set the PC IPv6 address to 2001:DB8::1/64, which is on the same network segment as GE1/0/1 of Firewall 1.
    Configure a static route from the PC to the destination network segment 2001:db8:1::/96, with the next hop address set to 2001:db8::2.
    Configure the DNS64 server IPv6 address on the PC.
  Configure an IPv4 address for the server. (The configuration method varies according to the server operating system. The detailed configuration procedure is not provided here.)
    Set the IPv4 address of the server to 1.1.1.2/24, which is on the same network segment as GE1/0/2 of Firewall 1.

## Slide 44: Translation Technology: IVI
The IVI stateless address translation technology translates an IPv4 address segment (IVI4 addresses) reserved by carriers into a special IPv6 address segment (IVI6 addresses embedded with IPv4 addresses).
Users with IVI6 addresses can directly access the global IPv6 network, and access the global IPv4 network after their IVI6 addresses are translated into IVI4 addresses by an IVI gateway.
IVI6 address format:
IPv6
IPv6 user
IVI DNS
IPv6 Internet
IPv6 server
IPv4 Internet
IPv4 server
IPv6 data
IPv4 data
IVI gateway
IVI6 address
IVI6 address
IVI6 address
IVI4 address
IVI Prefix
FF
Suffix
0
IPv4 Address
31
39
71
127
The first 32 bits are an IVI prefix, which is an IPv6 address prefix, and the last eight bits are fixed at FF.
The 41st to 72nd bits are an embedded IPv4 address.
The value of Suffix is all 0s.
Overview
IPv6 over IPv4
6PE
6VPE
NAT64
IPv4 over IPv6
IVI
Notes: IVI supports communication requests initiated by both IPv6 and IPv4 hosts.
The following uses access from an IVI6 host to a global IPv4 host as an example:
  In this scenario, stateless IPv6 address autoconfiguration cannot be used due to the special IVI6 address format. Therefore, the IVI6 host obtains the IVI6 address, default gateway address, and DNS server address through static configuration or DHCPv6 Options.
  The IVI6 host sends an AAAA query request to the dual-stack IVI DNS server. This DNS server stores the IVI4 addresses of IVI servers and their corresponding IVI6 addresses. When receiving the AAAA query request, the IVI DNS server sends an AAAA query request to the target network. If no AAAA record exists, the IVI DNS server sends an A query request, converts the obtained A record into an AAAA record according to the IVI mapping rule, and returns the AAAA record to the IVI6 host.
  The IVI6 host sends a data packet. When receiving this data packet, the IVI gateway statelessly converts the packet into an IPv4 packet. During address translation, the IPv4 address embedded in the IVI6 address is extracted and used as the source address in the IPv4 header. During header encapsulation, the Stateless IP/ICMP Translation (SIIT) algorithm is used.
  The resulting IPv4 data packet is routed to the IPv4 network, thereby implementing access from the IVI6 host to the IPv4 host.
IVI restrictions: The IPv6 addresses of hosts and servers must be planned and configured in compliance with the IVI format.

## Slide 45
(Multiple-answer question) Which of the following technologies can be used to carry IPv6 service traffic on an IPv4 WAN? ( )
  GRE tunneling
  6PE
  NAT64
  6VPE
Notes: ABD

## Slide 46
IPv6 can provide a large number of network address resources, making it a key to implementing Internet of Everything (IoE) and promoting the digital, network-based, and intelligent development of production and life. The IPv6-based next-generation Internet is an inevitable trend of Internet evolution and upgrade.
In the early stage of IPv4-to-IPv6 transition, IPv4 networks are widely deployed, whereas IPv6 networks are siloed networks scattered around the world. Tunneling technologies can be used to create tunnels over IPv4 networks, so as to connect these siloed IPv6 networks. Address translation technologies can also be used to translate between IPv6 and IPv4 addresses and protocols for bidirectional communication.
This course mainly describes the fundamentals and applications of transition technologies during IPv6 network evolution, including IPv6 over IPv4 tunneling, 6PE, 6VPE, IPv4 over IPv6 tunneling, NAT64, and IVI.