## Slide 1
Datacom
General
V1.0
Wu Yue/WX291773
2020.05.30
He Junjian/WX580230
New
Wu Yue/WX291773
2021.9.18
He Junjian/WX580230
Update

## Slide 2: QoS Fundamentals

## Slide 3
With continuous development of networks, the network scale and traffic types increase continuously. As a result, Internet traffic increases sharply, network congestion occurs, the forwarding delay increases, and even packet loss occurs. In this case, the service quality deteriorates or even services are unavailable. To deploy real-time and non-real-time services on the IP network, network congestion must be resolved. The commonly used solution is to increase the network bandwidth. However, this solution is not ideal considering the network construction cost.
Quality of service (QoS) is introduced in this situation. At limited bandwidth, QoS uses a "guaranteed" policy to manage network traffic and provides different priority services for different traffic.
This course describes QoS fundamentals.

## Slide 4
On completion of this course, you will be able to:
  Describe the QoS background.
  Describe QoS types.
  Describe the implementation of the QoS DiffServ model.
  Describe application scenarios of different QoS functions.
  Describes basic configuration of QoS.
  Describe HQoS fundamentals.
  Describe basic configuration of HQoS.

## Slide 5
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 6: "Best-Effort" Traditional Network
When the IP network emerges, there is no QoS guarantee.
You only know that the packets have been sent out. Whether the packets can be received and when the packets can be received are unknown.
Undifferentiated treatment
First In First Out (FIFO)
Notes: On the traditional IP network, each network device handles all packets in an undifferentiated manner and follows the First In First Out (FIFO) rule to transmit packets. The devices transmit packets to the destination in best-effort (BE) mode, but the BE mode cannot ensure the performance such as delay and reliability.

## Slide 7: QoS Background
With continuous technology improvement and fierce product competition, users have increasingly higher requirements on the network quality.
High-definition image quality and high network speed
Good signal quality
Poor image quality, low network speed, and frame freezing
Poor signal quality
Notes: With the emergence of new applications on IP networks, new requirements are raised to QoS of IP networks.

## Slide 8: Overview of QoS
Live streaming
Video communication
Email
FTP
How to allocate bandwidth?
How to provide services?
QoS:
QoS is designed to provide different service quality according to networking requirements.
Factors affecting QoS:
Bandwidth
Latency
Jitter
Packet loss rate
Availability
Notes: To support voice, video, and data services of different requirements, the network is required to distinguish different communication types before providing corresponding QoS.
  For example, real-time services such as Voice over IP (VoIP) demand shorter latency. A long latency for packet transmission is unacceptable. Email and the File Transfer Protocol (FTP) services are comparatively insensitive to the latency.
To support voice, video, and data services of different requirements, the network is required to distinguish different communication types before providing corresponding QoS.
  The BE mode of traditional IP networks cannot identify and distinguish various communication types on the networks. This distinguishing capability is the premise for providing differentiated services. The BE mode cannot satisfy application requirements, so QoS is introduced.
What is QoS?

## Slide 9
Notes: QoS is designed to provide different service quality according to networking requirements. Example:
  The bandwidth used by FTP on the backbone network can be limited, and database access can be given a higher priority.
  For an ISP, its users may transmit voice, video, or other real-time services. QoS enables the ISP to differentiate these packets and provide different services.
  QoS can provide bandwidth and low delay guarantee for time-sensitive multimedia services, and other services on the network do not affect these time-sensitive services.
Which factors affect QoS?
  Bandwidth: indicates the transfer speed of IP packets on a network. It can be the average value or peak value. — Bandwidth competition can be resolved by increasing the bandwidth. However, the bandwidth cannot be increased infinitely.
  Latency: indicates the round trip time (RTT) of an IP packet between two nodes on a network. — Delay-sensitive traffic, such as video and voice traffic
  Jitter: indicates the change in the latencies of different packets which are in the same data stream and transferred in the same direction. — It is related to the latency. If the latency is short, the jitter range is small, which has a great impact on real-time services such as voice and video services.
  Packet loss rate: indicates the allowed maximum packet loss rate when a service is transmitted on a network. — It is used to measure the network reliability. A small number of lost packets have little impact on services, but a large number of lost packets severely affect the transmission efficiency.
  Availability: indicates the availability of a connection between a user and the IP service, including the connection setup time and holding time.

## Slide 10: QoS Service Models
QoS provides three
service models:
Best-Effort (BE) model
Integrated Services (IntServ) model
Differentiated Services (DiffServ) model

## Slide 11: BE Model
An application can send any number of packets at any time.
The network then makes the best effort to transmit the packets.
No guarantee of performance in terms of delay and reliability
！
Undifferentiated treatment
FIFO
Notes: The BE model is the simplest service model in which an application can send any number of packets at any time without obtaining approval or notifying the network.
The network then makes the best effort to transmit the packets but provides no guarantee of performance in terms of delay and reliability.
The BE model is the default service model for the Internet and applies to various network applications, such as the File Transfer Protocol (FTP) and email. It uses FIFO queues.

## Slide 12: IntServ Model
Before sending packets, an application needs to apply for specific services through signaling.
After receiving a resource request from an application, the network reserves resources for each information flow by exchanging RSVP signaling information.
Complex implementation and waste of resources
！
Live streaming
Video communication
… …
Reserve 1 Mbit/s bandwidth
Reserve 1 Mbit/s bandwidth
I require 1 Mbit/s bandwidth.
Notes: The IntServ model is a comprehensive service model to meet various QoS requirements.
Before sending packets, an application needs to apply for specific services through signaling. This request is sent through RSVP. RSVP applies for network resources for an application before the application starts to send packets.
Once the network determines to allocate resources to the application, the network maintains a state for each flow (determined by IP addresses, port numbers, and protocol numbers at both ends), and performs packet classification, traffic policing, queuing, and scheduling based on the state. After receiving the acknowledgment message from the network (the application confirms that the network has reserved resources for the packets of the application), the application starts to send packets. As long as packets of the application are controlled within the range described by traffic parameters, the network promises to meet QoS requirements of the application.
Example: If you want to reserve a vehicle, you need to apply for a service in advance and reserve resources when resources are sufficient.
However, the vehicle service vendor has to maintain a large number of booking information.
Disadvantage: The implementation of the IntServ model is complex. When no traffic is transmitted, the bandwidth is still exclusively occupied, and the usage is low. This solution requires that all end-to-end nodes support and run the RSVP protocol.

## Slide 13: DiffServ Model
Traffic on a network is classified into multiple classes, and a corresponding processing behavior is defined for each class, so that the traffic has different forwarding priorities, packet loss rates, and delays.
DS domain
DS edge node
DS node
Live streaming
Video communication
FTP
Branch
Live streaming
Video communication
FTP
HQ
Traffic classification and marking
CoS Mapping
Queue scheduling
1
2
3
Notes: DiffServ is a multi-service model and can satisfy different QoS requirements. Currently, this model is widely used on IP networks.
Before sending a packet, the application does not need to notify the network to reserve resources for it. In the DiffServ model, the network does not need to maintain the status of each flow. Instead, it provides specific services based on precedence fields of packets (for example, the DS field in the IP header).
The DiffServ model classifies network traffic into multiple classes for differentiated processing. To be specific, the DiffServ model implements traffic classification first and allocates different identifiers to different classes of packets. After a network node receives these packets, it simply identifies these identifiers and processes packets based on the actions corresponding to these identifiers.
There is an analogy between the DiffServ model and train ticket service system. A train ticket marks the service that you book: soft sleeper, hard sleeper, hard seat, or no seat. You get on a train and enjoy the specific service marked in your ticket. On an IP network, an identifier is to a packet as a train ticket is to a passenger.
In addition to traffic classification and marking, the DiffServ model provides the queuing mechanism. When network congestion occurs on a device, the device buffers packets in queues. The device sends the packets out of queues when network congestion is relieved.

## Slide 14: Common QoS Technologies (DiffServ Model)
Common technologies
Traffic limiting
Traffic policing and traffic shaping are used to monitor the rate of traffic entering the network and limit the usage of traffic and resources.
It adjusts the network traffic to relieve network overload.
Congestion avoidance
Congestion management
It adjusts the scheduling sequence of packets to meet high QoS requirements of delay-sensitive services.
Notes: Rate limiting: Traffic policing and traffic shaping monitor the rate of traffic entering the network to limit the traffic and resource usage, providing better services for users.
Congestion avoidance and congestion management: When congestion occurs on a network, the device determines the sequence in which packets are forwarded according to a certain scheduling policy so key services are processed first. Or, the device proactively adjusts traffic to relieve network overload by discarding packets.

## Slide 15: QoS Data Processing (DiffServ Model)
Video
Voice
Data
Inbound interface
Traffic classification
Token bucket
Token
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Congestion avoidance
Enter a queue
Scheduling
Congestion management
Traffic shaping
Traffic policing
Outbound interface
Leave a queue
CAR
Notes: QoS technology provides the following functions:
  Traffic classification and marking: identify objects based on certain matching rules, which is the prerequisite for implementing differentiated services. They are usually applied to the inbound direction of an interface.
  Token bucket: is used to check whether traffic meets packet forwarding conditions.
  Traffic policing: monitors the volume of specific data traffic that arrives at network devices, and is usually applied to incoming traffic. When the traffic volume exceeds the maximum value, traffic limiting or punishment measures are taken to protect business interests and network resources of service providers.
  Congestion avoidance: Excessive congestion may damage network resources. Congestion avoidance monitors the usage of network resources. When congestion aggravates, congestion avoidance proactively adjusts traffic to relieve network overload by discarding packets. Congestion avoidance is generally applied to the outbound direction of an interface.
  Congestion management: is taken to solve the problem of resource competition. Packets are buffered in queues and a scheduling algorithm is used to determine the forwarding sequence of packets. Congestion management is usually applied to the outbound direction of an interface.

## Slide 16
Notes:   Traffic shaping: is a traffic control measure that initiatively adjusts the output speed of traffic. Traffic shaping enables the traffic to adapt to the network resources that can be provided by the downstream device to prevent packet loss and congestion. Traffic shaping is usually applied to the outbound direction of an interface.

## Slide 17
(Multiple-answer question) Which of the following service models are provided by QoS?（ ）
  DiffServ model
  IntServ model
  BE model
  Network service model
Notes: ABC

## Slide 18
QoS service models include the DiffServ, IntServ, and BE models.
The DiffServ model is the most commonly used QoS model. It provides rate limiting, congestion avoidance, and congestion management.

## Slide 19
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 20: QoS Data Processing
Video
Voice
Data
Inbound interface
Traffic classification
Token
CAR
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Enter a queue
Scheduling
Outbound interface
Leave a queue
Notes: Traffic classification and marking: identify objects based on certain matching rules, which is the prerequisite for implementing differentiated services. They are usually applied to the inbound direction of an interface.

## Slide 21: Why Are Traffic Classification and Traffic Marking Required?
Traffic classification and marking are the basis of QoS and the prerequisite for implementing differentiated services.
Video
Voice
Data
Inbound interface
Traffic classification
Provide different services
based on different types
Packets with different priorities
Traffic marking
Queue
Notes: To implement differentiated services, the traffic entering a DS domain needs to be classified according to certain rules, and then different services are provided for different types of traffic.
After packets are classified at the DS domain edge, intermediate nodes provide differentiated services for classified packets. The downstream node can accept the classification result of its upstream node or classifies packets based on its own criteria.
Traffic classification and marking are prerequisites for differentiated services.
  Traffic classification technology classifies packets into different types, and does not modify the data packets.
  Marking technology marks packets with different priorities, and modifies the data packets. Marking is classified into internal and external marking.
    Internal marking
    Sets the CoS and drop precedence of packets for internal processing on a device so that packets can be placed directly in specific queues.
    Setting the drop precedence of packets is also called coloring packets. When traffic congestion occurs, packets in the same queue are provided with differentiated buffer services based on colors.

## Slide 22
Notes:     External marking
    Sets or modifies the priority of packets so that the downstream device can provide services based on the changed priority. Modifying the packet priorities is also called re-marking.

## Slide 23: Behavior Aggregate Classification
802.1p
MPLS EXP
DSCP
Mapping
Service class
Color
Service class
Color
802.1p
MPLS EXP
DSCP
Mapping
SFU
Uplink direction
Different packets
use
different QoS priorities.
Packet header priority
CoS
of packets
on the device
Service class
Drop priority
of packets
on the device
Color
VLAN packet
MPLS packet
IP packet
BA classification
External priority
Internal priority
Downlink direction
Drop priority
Notes: BA classification allows the device to classify packets based on related values as follows: IP priority or DSCP value of IPv4 packets, TC value of IPv6 packets, EXP value of MPLS packets, and 802.1p value of VLAN packets. It is used to simply identify the traffic that has the specific priority or service classes for mapping between external and internal priorities.
BA classification confirms that the priority of incoming packets on a device is trusted and mapped to the service class and color based on a priority mapping table. The service class and color of outgoing packets are then mapped back to the priority.
Packets carry different types of precedence field depending on the network type. For example, packets carry the 802.1p value on a VLAN network, the EXP value on an MPLS network, and the DSCP value on an IP network. To provide differentiated services for different packets, the device maps the QoS priority of incoming packets to the scheduling precedence (also called service class) and drop precedence (also called color), and then performs congestion management based on the service-class and congestion avoidance based on the color. Before forwarding packets out, the device maps the service class and color of the packets back to the QoS priority, which provides a basis for other devices to process the packets.

## Slide 24: External Priority: VLAN Packet
802.1p
MPLS EXP
DSCP
Mapping
Service class
Color
Service class
Color
802.1p
MPLS EXP
DSCP
Mapping
SFU
Uplink direction
Different packets
use different
QoS priorities.
Packet header priority
VLAN packet
MPLS packet
IP packet
BA classification
External priority
Downlink direction
Dest add | Sour add | 802.1Q (PRI) | Length/Type | Data | FCS
TPID | PRI (3 bits) | CFI | VLAN ID
VLAN packet
Value range: 0–7
Notes: Eight service priorities (PRIs) are defined in the VLAN tag of the Ethernet frame header.

## Slide 25: External Priority: MPLS Packet
Mapping
Service class
Color
Service class
Color
Mapping
SFU
Uplink direction
Different packets
use different
QoS priorities
Packet header priority
BA classification
External priority
Downlink direction
MPLS packet
Link layer header | Label (EXP) | Layer 3 header | Layer 3 payload
802.1p
MPLS EXP
DSCP
VLAN packet
MPLS packet
IP packet
802.1p
MPLS EXP
DSCP
Label | EXP (3 bits) | S | TTL
Value range: 0–7
Notes: The EXP field in the label is used as the external priority of MPLS packets to differentiate service classes of data traffic.

## Slide 26: External Priority: IP Packet
Mapping
Service Class
Color
Service Class
Color
Mapping
SFU
Uplink direction
Different packets
use different
QoS priorities.
Packet header priority
BA classification
External priority
Downstream direction
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IP packet
Version | Len | ToS (IP Precedence/DSCP) | … | Protocol | FCS | IP-SA | IP-DA | Data
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IP precedence
DSCP
Value range: 0–7
Value range: 0–63
802.1p
MPLS EXP
DSCP
VLAN packet
MPLS packet
IP packet
802.1p
MPLS EXP
DSCP
Notes: Eight IP service types are defined in the Precedence field of the ToS field in an IPv4 packet header.
The ToS field in the IPv4 packet header is redefined as the Differentiated Services (DS) field. That is, the IP Precedence field is extended.

## Slide 27: Mapping Between External Priorities
Priority in descending order
802.1P | MPLS Exp | IP-Precedence | DSCP | DSCP Name |  |  |  | 
7 | 7 | 7 | 56-63 | CS | CS7 (56) |  |  | 
6 | 6 | 6 | 48-55 |  | CS6 (48) |  |  | 
5 | 5 | 5 | 40-47 | EF | EF (46) |  |  | 
4 | 4 | 4 | 32-39 | AF | AF4 | AF41 (34) | AF42 (36) | AF43 (38)
3 | 3 | 3 | 24-31 |  | AF3 | AF31 (26) | AF32 (28) | AF33 (30)
2 | 2 | 2 | 16-23 |  | AF2 | AF21 (18) | AF22 (20) | AF23 (22)
1 | 1 | 1 | 8-15 |  | AF1 | AF11 (10) | AF12 (12) | AF13 (14)
0 | 0 | 0 | 0-7 | BE | BE (0) |  |  | 

## Slide 28: Service Class
802.1p
MPLS EXP
DSCP
Mapping
Service class
Color
Uplink direction
Service class
of packets
on the device
Service class
VLAN packet
MPLS packet
IP packet
BA classification
Internal priority
Service Class
Color
Mapping
SFU
Downlink direction
802.1p
MPLS EXP
DSCP
CS | CS7
 | CS6
EF | EF
AF | AF4
 | AF3
 | AF2
 | AF1
BE | BE
Service class
determines the types of queues to which packets belong.
Priority in descending order
Queue
Notes: Service class, that is, queue
Service classes refer to the internal priorities of packets. Eight service class values are available: class selector 7 (CS7), CS6, expedited forwarding (EF), assured forwarding 4 (AF4), AF3, AF2, AF1, and best-effort (BE). Service classes determine the types of queues to which packets belong.
The priority of queues with a specific service class is calculated based on scheduling algorithms.
  If queues with eight service classes all use priority queuing (PQ) scheduling, queues are displayed in descending order of priority: CS7 > CS6 > EF > AF4 > AF3 > AF2 > AF1 > BE.
  If the BE queue uses PQ scheduling (this configuration is rare on live networks) but all the other seven queues use weighted fair queuing (WFQ) scheduling, the BE queue is of the highest priority.
  If the queues of eight service classes all use WFQ scheduling, their priorities are the same.

## Slide 29: Color
802.1p
MPLS EXP
DSCP
Mapping
Service class
Color
Uplink direction
Drop priority
of packets
on the device
Color
VLAN packet
MPLS packet
IP packet
BA classification
Service class
Color
Mapping
SFU
Downlink direction
802.1p
MPLS EXP
DSCP
Green
Yellow
Red
Priority in descending order
Color
The color of packets determines the order in which packets are dropped in a congested queue.
Notes: Color, referring to the drop priority of packets on a device, determines the order in which packets in one queue are dropped when traffic congestion occurs.
As defined by the Institute of Electrical and Electronics Engineers (IEEE), the color of a packet can be green, yellow, or red.
Drop priorities are compared based on the configured parameters. For example, if a maximum of 50% of the buffer is configured to store packets colored green, whereas a maximum of 100% of the buffer is configured to store packets colored red, the drop priority of packets colored green is higher than that of packets colored red.

## Slide 30: Mapping
Mapping from internal priorities to external priorities
802.1p
MPLS EXP
DSCP
Mapping
Uplink direction
VLAN packet
MPLS packet
IP packet
BA classification
Service class
Color
Mapping
SFU
Downlink direction
802.1p
MPLS EXP
DSCP
Service class
Color
DSCP |  |  |  | Service Class/Color |  |  | 
32-39 | 34 | 36 | 38 | AF | AF41 | AF42 | AF43
24-31 | 26 | 28 | 30 |  | AF31 | AF32 | AF33
16-23 | 18 | 20 | 22 |  | AF21 | AF22 | AF23
8-15 | 10 | 12 | 14 |  | AF11 | AF12 | AF13
Service Class/Color |  |  |  | DSCP |  |  | 
AF | AF41 | AF42 | AF43 | 32-39 | 34 | 36 | 38
 | AF31 | AF32 | AF33 | 24-31 | 26 | 28 | 30
 | AF21 | AF22 | AF23 | 16-23 | 18 | 20 | 22
 | AF11 | AF12 | AF13 | 8-15 | 10 | 12 | 14
Mapping from external priorities to internal priorities
Uplink mapping
Downlink mapping
Notes: A device maps the QoS priority to the service class and color for incoming packets and maps the service class and color back to the QoS priority for outgoing packets.

## Slide 31: Multi-field Classification
DS edge node
Live streaming
Video communication
FTP
HQ
Live streaming
Video communication
FTP
Branch
MF classification
MF classification classifies packets based on complex rules in a fine-grained manner, such as the 5-tuple (source IP address, source port number, protocol number, destination address, and destination port number).
Configure a traffic classifier
Configure a traffic behavior
Configure a traffic policy
Apply the traffic policy
Real-time services such as voice and video services are given the highest priority.
Template-based QoS
Notes: As networks rapidly develop, services on the Internet become increasingly diversified. Various services share limited network resources. In particular, multiple services use port number 80. Because of this increasing demand, network devices are required to possess a high degree of sensitivity for services, including an in-depth parsing of packets and a comprehensive understanding of any packet field at any layer. This level of sensitivity rises far beyond what BA classification can offer. MF classification can be deployed to help address this sensitivity deficit.
MF classification classifies packets based on complex rules in a fine-grained manner, such as the 5-tuple (source IP address, source port number, protocol number, destination address, and destination port number).

## Slide 32: Traffic Policy Overview
Data flow
Modular QoS command line interface (MQC) uses traffic policies.
A traffic policy is often bound to traffic classifiers and traffic behaviors. A traffic classifier is used to match data packets, and a traffic behavior is used to modify data packets.
Traffic policy
Traffic classifier
Traffic behavior
Traffic matching rule 1
Traffic matching rule 2
Traffic matching rule 3
OR
Traffic modification rule 1
Traffic modification rule 2
Traffic modification rule 3
Modification in sequence
Traffic classifier
Traffic behavior
Traffic matching rule 1
Traffic matching rule 2
Traffic matching rule 3
OR
Traffic modification rule 1
Traffic modification rule 2
Traffic modification rule 3
Modification in sequence
Traffic policy 1
Traffic policy 2
Execution in sequence

## Slide 33: Traffic Classification Process
DS edge node
DS node
Live streaming
Video communication
FTP
HQ
Live streaming
Video communication
FTP
Branch
DS node
DS edge node
MF classification
BA classification
Real-time services such as voice and video services are given the highest priority.
Notes: Requirement: The highest forwarding priority must be provided for real-time services such as voice and video services.
Implementation: The DS edge node obtains service traffic such as voice and video traffic through MF classification and maps the traffic to the corresponding priorities. It processes the remaining traffic through BA classification.

## Slide 34: Configuring MF Classification
DS edge node
DS node
Typically, the traffic received by the DS edge node is not classified, so complex traffic classification is configured on the DS edge node. The configuration roadmap is as follows:
  Configure a traffic classifier to match traffic.
  Configure a traffic behavior to define an action taken on the matched traffic.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to the inbound direction of the interface on the DS edge node.
DS domain
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on traffic characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
remark [dscp-name | 8021p-value | EXP | … ] //Re-mark the QoS field of traffic.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] [inbound | outbound] //Apply the traffic policy to the inbound direction of an interface.

## Slide 35: Checking the MF Classification Configuration
After MF classification is configured, you can run the following commands to check the configuration.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.

## Slide 36: (Optional) Modifying the BA Classification Configuration
Specify the packet priority trusted on an interface.
Configure a priority mapping table.
DS edge node
DS node
Based on the priority mapping table, BA classification maps data with the specific QoS field to the internal priority.
The priority mapping table can be modified as required. The roadmap is as follows:
  Specify the packet priority trusted on an interface.
  Configure a priority mapping table.
DS domain
system-view
interface [interface-type interface-num] //Enter the interface view.
trust [8021p | dscp] //Specify the priority to be trusted.
system-view
qos map-table [ dot1p-dot1p | dot1p-dscp | dot1p-lp | dscp-dot1p | dscp-dscp | dscp-lp ] //Enter the priority mapping table view.
input [input-value1] output [output-value] //Configure mappings in the priority mapping table.

## Slide 37: Checking the Priority Mapping Configuration
After the priority mapping configuration is modified, you can run the following commands to check the configuration.
system-view
display qos map-table [ dot1p-dot1p | dot1p-dscp | dot1p-lp | dscp-dot1p | dscp-dscp | dscp-lp ] //Check the mapping between priorities.

## Slide 38
(True or false) MF classification is generally deployed in the inbound direction of the DS edge node.( )
  True
  False
(Multiple-answer question) Which of the following parameters are used to mark the QoS priority of data packets?( )
  EXP
  802.1p
  DSCP
  IP precedence
Notes: A
ABCD

## Slide 39
The DiffServ model must mark packets for differentiating them. Generally, MF classification is used to mark incoming traffic on edge devices in a DS domain, and BA classification is used to mark incoming traffic on devices in a DS domain.
Tags can be added to multiple types of data packet headers.
  The Pri bit (802.1p priority) in the VLAN header is used to mark the QoS priority.
  The EXP bit in the MPLS header is used to mark the QoS priority.
  The TOS bit (DSCP/IP precedence) in the IP header is used to mark the QoS priority.

## Slide 40
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 41: QoS Data Processing
Monitors the traffic entering the device to ensure that network resources are not abused.
Traffic classification
CAR
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Enter a queue
Scheduling
Outbound interface
Leave a queue
Traffic policing
Traffic shaping
Traffic policing
Controls the rate of outgoing packets so that packets are sent at an even rate.
Traffic shaping
Function
Monitor network traffic at the network edge.
Specify the bandwidth usage for different incoming and outgoing traffic so that different services are allocated different bandwidths.
Video
Voice
Data
Inbound interface
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: This course describes two rate limiting technologies: traffic policing and traffic shaping.
Traffic policing: If the traffic rate of a connection exceeds the specifications on an interface, traffic policing allows the interface to drop excess packets or re-mark the packet priority to protect network resources and protect carriers' profits. An example of this process is restricting the rate of HTTP packets to 50% of the network bandwidth.
Traffic shaping: allows the traffic rate to match that on the downstream device. When traffic is transmitted from a high-speed link to a low-speed link or a traffic burst occurs, the inbound interface of the low-speed link is prone to severe data loss. To prevent this problem, traffic shaping must be configured on the outbound interface of the device connecting to the high-speed link.

## Slide 42: Traffic Limiting Technology
Video
Voice
Data
Inbound interface
Traffic classification
CAR
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Enter a queue
Scheduling
Outbound interface
Leave a queue
Traffic policing
Traffic shaping
Token
Token bucket
Token bucket technology
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: Both traffic policing and traffic shaping use the token bucket technology.
  Token bucket: A token bucket is used to check whether traffic meets packet forwarding conditions.

## Slide 43: Single-Rate-Single-Bucket Mechanism
B < Tc?
Size of an arriving packet (B)
Yes (Tc = Tc-B)
No (Tc remains unchanged)
Token
CIR
CBS
Bucket C
Initial number of tokens (Tc) = CBS
Discard packets in the case of overflow
Committed Information Rate (CIR):
  indicates the rate at which tokens are put into bucket C, in kbit/s.
Committed burst size (CBS):
  indicates the maximum volume of burst traffic that bucket C allows before the rate of some traffic exceeds the CIR, that is, the capacity of bucket C. The value is expressed in bytes.
The data packet is marked red and discarded by default.
The data packet is marked green and forwarded by default.
The single-rate-single-bucket mechanism does not allow burst traffic. Only committed traffic is allowed.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: When a packet arrives, the device compares the packet with the number of tokens in the bucket. If there are sufficient tokens, the packet is forwarded (one token is associated with 1-bit forwarding permission). If there are no enough tokens, the packet is discarded or buffered.
Tc and Te refer to the numbers of tokens in buckets C and E, respectively. The initial values of Tc and Te are respectively the CBS and EBS.
In color-blind mode (B indicates the size of an arriving packet):
  If B is less than or equal to Tc, the packet is marked green, and Tc decreases by B.
  If B is greater than Tc, the packet is marked red, and Tc remains unchanged.

## Slide 44: Single-Rate-Two-Bucket Mechanism
B < Tc ?
Size of an arriving packet (B)
No
Tc<B<Te?
No (Tc and Te remain unchanged)
CBS
Token
Bucket C
Bucket E
EBS
CIR
Token overflow
Initial number of tokens
Bucket C: Tc = CBS
Bucket E: Te = EBS
Yes (Tc = Tc-B)
Yes (Te = Te-B)
CIR:
  Indicates the rate at which tokens are put into bucket C, in kbit/s.
CBS:
  Indicates the maximum volume of burst traffic that bucket C allows before the rate of some traffic exceeds the CIR, that is, the capacity of bucket C. The value is expressed in bytes.
Excess burst size (EBS):
  Indicates the maximum volume of excess burst traffic that bucket E allows. The value is expressed in bytes.
The data packet is marked red and discarded by default.
The data packet is marked green and forwarded by default.
The data packet is marked yellow and forwarded by default.
The single-rate-two-bucket mechanism allows transient burst traffic.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: When a packet arrives, the device compares the packet with the number of tokens in the bucket. If there are sufficient tokens, the packet is forwarded (one token is associated with 1-bit forwarding permission). If there are no enough tokens, the packet is discarded or buffered.
Tc and Te refer to the numbers of tokens in buckets C and E, respectively. The initial values of Tc and Te are respectively the CBS and EBS.
In color-blind mode (B indicates the size of an arriving packet):
  If B is less than or equal to Tc, the packet is marked green and Tc decreases by B.
  If B is greater than Tc and less than or equal to Te, the packet is marked yellow and Te decreases by B.
  If B is greater than Te, the packet is marked red, and Tc and Te remain unchanged.

## Slide 45: Two-Rate-Two-Bucket Mechanism
Initial number of tokens
Bucket P: Tp = PBS
Bucket C: Tc = CBS
Bucket P
Discard packets in the case of overflow
PBS
PIR
CBS
Token
Discard packets in the case of overflow
Bucket C
CIR
Token
Peak Information Rate (PIR):
  Indicates the rate at which tokens are put into bucket P, that is, the maximum traffic rate that bucket P allows. The PIR is greater than the CIR. The value is expressed in kbit/s.
Peak burst size (PBS):
  Indicates the capacity of bucket P, that is, the maximum volume of burst traffic that bucket P allows. The PBS is greater than the CBS. The value is expressed in bytes.
CIR:
  Indicates the rate at which tokens are put into bucket C, in kbit/s.
CBS:
  Indicates the maximum volume of burst traffic that bucket C allows before the rate of some traffic exceeds the CIR, that is, the capacity of bucket C. The value is expressed in bytes.
The two-rate-two-bucket mechanism allows long-term burst traffic.
The data packet is marked red and discarded by default.
The data packet is marked yellow and forwarded by default.
The data packet is marked green and forwarded by default.
B > Tp?
Size of an arriving packet (B)
Yes (Tc and Tp remain unchanged)
No
Tp > B > Tc?
No (Tc = Tc-B)
Yes (Tp = Tp-B)
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: The two rate three color marker (trTCM) algorithm focuses on the traffic burst rate and checks whether the traffic rate conforms to the specifications. Therefore, traffic is measured based on bucket P and then bucket C.
Tc and Tp refer to the number of tokens in buckets C and P, respectively. The initial values of Tc and Tp are respectively the CBS and PBS.
In color-blind mode (B indicates the size of an arriving packet):
  If B is greater than Tp, the packet is marked red and Tc and Tp remain unchanged.
  If B is greater than Tc and less than or equal to Tp, the packet is marked yellow and Tp decreases by B.
  If B is less than or equal to Tc, the packet is marked green, and Tp and Tc decrease by B.

## Slide 46: What Is Traffic Policing?
Traffic policing uses the committed access rate (CAR) to control traffic. CAR uses the token bucket algorithm to evaluate the traffic rate and implements preset policing actions based on the evaluation result.
Implementation of traffic policing
LAN
WAN
High-speed link
Low-speed link
Data flow:
100 Mbit/s
Traffic policing
By monitoring the specifications of a certain type of traffic that enters the network, you can limit the traffic within an allowed range. If the traffic of a connection is too heavy, the packets are discarded or the priority of the packets is re-set to protect network resources. Traffic policing can be configured in inbound and outbound directions of an interface.
Packet rate
Time
CIR
When traffic policing is used,
packets exceeding the rate limit may be discarded or their priorities may be lowered.
Traffic policing not configured
Interface bandwidth is
only 2 Mbit/s.
Configure traffic policing
in the inbound direction of the interface.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: In the figure:
  An edge network device connects a wide area network (WAN) and a local area network (LAN). The LAN bandwidth (100 Mbit/s) is higher than the WAN bandwidth (2 Mbit/s).
  When a LAN user attempts to send a large amount of data to a WAN, the edge network device is prone to traffic congestion. Traffic policing can be configured on the edge network device to restrict the traffic rate, preventing traffic congestion.
Characteristics of traffic policing:
  Drops excess traffic over the specifications or re-marks such traffic with a lower priority.
  Consumes no additional memory resources and brings no delay or jitter.
  Packet loss may result in packet retransmission.
  Traffic can be re-marked.

## Slide 47: CAR
CAR uses token buckets to measure traffic and determines whether a packet conforms to the specification.
Token bucket modes
Single-rate-single-bucket
Single-rate-two-bucket
Two-rate-two-bucket
The device marks the packet red, yellow, or green based on the metering result using the token bucket.
Green indicates that the packets comply with the specifications and are directly forwarded.
Yellow indicates that temporary burst traffic is allowed although it does not comply with specifications. After the traffic is re-marked, the priority is reduced and the traffic is forwarded in BE mode.
Red indicates that the packet rate is high and does not comply with the specifications. Therefore, the packets are discarded.
Arriving packets
Traffic classification
Token bucket
Packets do not match rules.
Packets are forwarded at the original rate.
(Traffic policing is not required.)
Packets match rules.
Partially compliant
Compliant
Exceeding
Remark
Forward
Discard
Traffic policing actions
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: Traffic policing uses CAR to control traffic. CAR uses token buckets to measure traffic and determines whether a packet conforms to the specification.
CAR has the following two functions:
  Rate limiting: Only packets allocated enough tokens are allowed to pass so that the traffic rate is restricted.
  Traffic classification: Packets are marked internal priorities, such as the service class and drop priority, based on the measurement performed by token buckets.
CAR process:
  When a packet arrives, the device matches the packet against matching rules. If the packet matches a rule, the device uses token buckets to meter the traffic rate.
  The device marks the packet red, yellow, or green based on the metering result using the token bucket. Red indicates that the traffic rate exceeds the specifications. Yellow indicates that the traffic rate exceeds the specifications but is within an allowed range. Green indicates that the traffic rate is conforming to the specifications.
  The device drops packets marked red, re-marks and forwards packets marked yellow, and forwards packets marked green.

## Slide 48
Notes: Three token bucket modes can be used.
  To control the traffic rate, use single-rate-single-bucket.
  To differentiate traffic bursts at limited bandwidth, use the single-rate-two-bucket mechanism. Note that traffic marked yellow must be processed differently from traffic marked green. Otherwise, the implementation of the single-rate-two-bucket mechanism is the same as that of the single-rate-single-bucket mechanism.
  To control the traffic rate and check whether the traffic rate exceeds the CIR or PIR, use two-rate-two-bucket. Note that traffic marked yellow must be processed differently from traffic marked green. Otherwise, the implementation of the two-rate-two-bucket mechanism is the same as that of the single-rate-single-bucket mechanism.

## Slide 49: Application Scenario of Traffic Policing
LAN
WAN
Traffic direction
Video
Data
Voice
App 1
Interface-based traffic policing
Class-based traffic policing
Application of traffic policing
It is generally used to control incoming traffic and prevent excess traffic from entering the device.
It is recommended for delay-sensitive traffic (such as video and voice traffic).
Configure traffic policing
in the inbound direction of the interface.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: Voice, video, and data services are transmitted on an enterprise network. When a large amount of traffic enters the network, congestion may occur due to insufficient bandwidth. Different guaranteed bandwidth must be provided for the voice, video, and data services in descending order of priority. In this situation, traffic policing can be configured to provide the highest guaranteed bandwidth for voice packets and lowest guaranteed bandwidth for data packets. This configuration ensures preferential transmission of voice packets during congestion.
Interface-based traffic policing
  Interface-based traffic policing controls all traffic that enters an interface and does not identify the packet types. (based on the interface)
Class-based traffic policing
  Class-based traffic policing controls the rate of one or more types of packets that enter an interface. (based on traffic classification)

## Slide 50: Configuring Interface-based Traffic Policing
Configure interface-based traffic policing.
DS edge device
DS node
Typically, traffic policing is performed in the inbound direction of a device. Traffic policing can be deployed on the terminal side or in the inbound direction of an egress device as required. Traffic policing can be configured based on interfaces or MQC.
The configuration roadmap of interface-based traffic policing is as follows:
  Set the maximum bandwidth for traffic policing on an interface, select the traffic to be policed, and adjust the behavior to be taken on the excess traffic.
DS domain
system-view
interface [interface-type interface-num] //Enter the interface view.
qos car [ inbound | outbound ] [ acl acl-number | destination-ip-address | source-ip-address ] cir [cir-value] [ pir pir-value ] [ cbs cbs-value pbs pbs-value ] //Configure traffic policing for specific traffic in the inbound or outbound direction of an interface. The CIR must be configured. The CIR indicates the maximum committed rate of traffic policing. If the PIR is not configured, it is equal to the CIR. In this case, the traffic rate cannot be higher than the CIR.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping

## Slide 51: Configuring MQC-based Traffic Policing
DS edge device
DS node
MQC can be used to implement traffic policing in a more refined manner. The device can control traffic and allocate different bandwidths based on the 5-tuple and QoS value of the data packet.
The configuration roadmap is as follows:
  Configure a traffic classifier to match traffic.
  Configure a traffic behavior to define actions taken for packets.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to an interface.
DS domain
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on traffic characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
car cir [cir-value] [ pir pir-value ] [ cbs cbs-value pbs pbs-value ] //Set the CIR and PIR.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] [inbound | outbound] //Apply the traffic policy to the inbound direction of an interface.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping

## Slide 52: Checking the Traffic Policing Configuration
After interface-based traffic policing is configured, you can run the following commands to check the configuration.
system-view
display qos car statistics interface [interface-type interface-num] [inbound | outbound] //Check statistics on forwarded and discarded packets on the interface.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.
After MQC-based traffic policing is configured, you can run the following commands to check the configuration.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping

## Slide 53: What Is Traffic Shaping?
Traffic shaping
Traffic shaping is a measure to adjust the traffic rate sent from an interface.
Traffic shaping is configured on the outbound interface of an upstream device so that irregular traffic can be transmitted at an even rate, preventing transient traffic congestion on the downstream device.
Implementation of traffic shaping
Traffic shaping is implemented using the buffer and token bucket.
Token bucket mode: single-rate-single-bucket
Assessment result: compliant (green), non-compliant (red)
Packet rate
Time
CIR
Traffic shaping not deployed
LAN
WAN
High-speed link
Low-speed link
Data flow:
100 Mbit/s
Traffic shaping deployed
Interface bandwidth
is 1 Gbit/s.
Interface bandwidth
is only 2 Mbit/s.
Outbound direction of the interface
Traffic shaping
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: Generic Traffic Shaping (GTS)
  When traffic is transmitted from a high-speed link to a low-speed link or a traffic burst occurs, the inbound interface of the low-speed link is prone to severe data loss. To prevent this problem, configure traffic shaping on the outbound interface of the device connecting to the high-speed link.
  When packets are sent at a high speed, they are cached and then evenly sent through the token bucket.
Characteristics of traffic shaping:
  Buffers excess traffic over the specifications.
  Consumes memory resources for buffering excess traffic and brings delay and jitter.
  Packet loss rarely occurs, so packets are seldom retransmitted.
  Traffic re-marking is not supported.
Token bucket mode: single-rate-single-bucket — The evaluation result can be either green or red.

## Slide 54: Implementation of Traffic Shaping (1)
Queue
Shaping?
Scheduling
Leave a queue
Forward
No
Compliant
Token bucket
Exceeding
The data packets that are leaving queues are still forwarded.
When packets in a queue are transmitted at a rate exceeding the specifications, the queue is marked unscheduled and will be scheduled when the bandwidth is available.
Yes
Queue-based traffic shaping
Queue-based traffic shaping
Applies to each queue on an outbound interface.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: When packets leave queues, the packets that do not need to be shaped are forwarded. The packets that need to be shaped are measured against token buckets.
  If the packet rate conforms to the rate limit, the packet is marked green and forwarded.
  If the rate of a data packet exceeds the threshold, the data packet is still forwarded. In this case, the status of the queue where the data packet is located is changed to unscheduled, and the queue is scheduled when the token bucket is filled with new tokens. After the queue is marked unscheduled, more packets can be put into the queue, but excess packets over the queue capacity are dropped. Therefore, traffic shaping allows traffic to be sent at an even rate but does not provide zero-packet-loss guarantee.

## Slide 55: Implementation of Traffic Shaping (2)
Queue 3
Scheduling
Leave a queue
Token bucket
If the packet rate exceeds the rate limit,
the interface stops scheduling and waits for sufficient tokens to continue scheduling.
Interface-based traffic shaping
Queue 1
Queue 2
Queue N
…
Interface-based traffic shaping
Forward the packet if the packet conforms to the rate limit
All queues on an interface
Limits the total rate of all packets sent by an interface. Traffic shaping is performed on the outbound interface, regardless of packet priorities.
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping
Notes: When packets leave queues, all queues are measured together against token buckets.
  If the packet rate conforms to the rate limit, the packet is marked green and forwarded.
  If the packet rate exceeds the threshold (that is, tokens in the token bucket are insufficient), the packet is marked red. In this case, the interface stops scheduling and continues to schedule the packets when there are sufficient tokens.

## Slide 56: Application Scenario of Traffic Shaping
Traffic shaping is generally used in the outbound direction of an interface and is mainly used to limit the traffic rate. It is recommended for packet loss-sensitive traffic (such as Internet access and service download).
On an enterprise network, the enterprise headquarters is connected to branches through private lines on an ISP network. Branches connect to the Internet through the headquarters.
If all branches connect to the Internet at the same time, a large amount of web traffic sent from the headquarters to the Internet causes network congestion. As a result, some web traffic is discarded.. As shown in the figure, to prevent web traffic loss, traffic shaping can be configured before traffic sent from enterprise branches enters the enterprise headquarters.
HQ
Traffic direction
Branch 1
Branch 2
Internet
ISP
Configure
traffic shaping in the outbound direction of an interface.
Uplink mapping
Traffic Limiting
Token Bucket
Traffic Policing
Traffic Shaping

## Slide 57: Configuring Interface-based Traffic Shaping
Configure interface-based traffic shaping.
DS edge node
DS node
DS domain
Traffic shaping can be configured only in the outbound direction of a device. It falls into interface-based, queue-based, and MQC-based traffic shaping.
Interface-based traffic shaping has a large granularity. The configuration roadmap is as follows:
  Deploy traffic shaping in the outbound direction of an interface and configure the maximum bandwidth.
system-view
interface [interface-type interface-num] //Enter the interface view.
qos gts cir [cir-value] [ cbs cbs-value ] //Configure traffic shaping in the outbound direction of an interface. The CIR indicates the maximum traffic shaping rate. You can configure the CBS as required to control the size of the token bucket. The CIR must be configured.

## Slide 58: Configuring Queue-based Traffic Shaping
Create a queue profile and configure queue shaping.
Apply the queue profile to an interface.
DS edge node
DS node
DS domain
To shape packets in each queue on an interface, configure a queue profile and apply it to the interface.
You can set different traffic shaping parameters for queues with different priorities to provide differentiated services. The configuration roadmap is as follows:
  Create a queue profile.
  Configure queue shaping.
  Apply the queue profile to an interface.
system-view
interface [interface-type interface-num] //Enter the interface view.
qos queue-profile [queue-profile-name] //Create a queue profile.
queue [start-queue-index] to [end-queue-index ] gts cir [cir-value] [ cbs cbs-value ] //Configure traffic shaping for a specified queue in the outbound direction and set the CIR.
system-view
interface [interface-type interface-num] //Enter the interface view.
qos queue-profile [queue-profile-name] //Apply the queue profile to the interface.

## Slide 59: Configuring MQC-based Traffic Shaping
DS edge node
DS node
DS domain
MQC-based traffic policing uses traffic classifiers to implement differentiated services.
The configuration roadmap is as follows:
  Configure a traffic classifier to match traffic.
  Configure a traffic behavior to define an action for packets.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to an interface in the outbound direction.
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on traffic characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
gts cir [cir-value] | pct [pct-value] //Configure traffic shaping based on the maximum traffic rate or the percentage of the occupied interface bandwidth.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] [inbound | outbound] //Apply the traffic policy to the interface in the outbound direction.

## Slide 60: Checking the Traffic Shaping Configuration
After queue-based traffic shaping is configured, you can run the following commands to check the configuration.
After MQC-based traffic shaping is configured, you can run the following commands to check the configuration.
system-view
display qos queue-profile [ queue-profile-name ] //Check the queue profile configuration.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.

## Slide 61
(True or false) Traffic shaping caches excess traffic by default, and traffic policing discards excess traffic by default.( )
  True
  False
(Multiple-answer question) How many modes of token buckets are used to measure traffic?( )
  Single-rate-single-bucket
  Three-rate-two-bucket
  Single-rate-two-bucket
  Two-rate-two-bucket
Notes: A
ACD

## Slide 62
There are two traffic limiting technologies: traffic policing and traffic shaping.
Traffic policing discards excess traffic by default. It can be deployed in inbound and outbound directions of a device.
Traffic shaping caches excess traffic by default. It can be deployed only in the outbound direction of a device.
The device uses token buckets to measure traffic. There are three modes of token buckets:
  The single-rate-single-bucket mechanism can be used together with traffic policing and traffic shaping.
  The single-rate-two-bucket mechanism can be used only with traffic policing, and is mainly used in scenarios where burst traffic occurs occasionally.
  The two-rate-two-bucket can be used only with traffic policing, and is mainly used in scenarios with long-term burst traffic.

## Slide 63
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 64: QoS Data Processing
Traffic classification
CAR
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Enter a queue
Scheduling
Outbound interface
Leave a queue
Video
Voice
Data
Inbound interface
Token
Token bucket
Congestion avoidance
What is congestion?
Notes: Congestion avoidance: Excessive congestion may damage network resources. Congestion avoidance monitors the usage of network resources. When congestion aggravates, congestion avoidance adjusts traffic to relieve network overload by discarding packets. Congestion avoidance is generally applied to the outbound direction of an interface.

## Slide 65: Background of Congestion Occurrence
2 Mbit/s
WAN
LAN
2 Mbit/s
Data flow
10 Mbit/s
LAN
Congestion point
100 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s
Aggregation problem
High-speed link
Low-speed link
100 Mbit/s
10 Mbit/s
Bandwidth mismatch
Notes: Traffic congestion occurs when multiple users compete for the same resources (such as the bandwidth and buffer) on the shared network.
  For example, a user on a LAN sends data to a user on another LAN through a WAN. The WAN bandwidth is lower than the LAN bandwidth. Therefore, data cannot be transmitted at the same rate on the WAN as that on the LAN. Traffic congestion occurs on the router connecting the LAN and WAN.
Congestion often occurs in the following situations:
  Traffic rate mismatch: Packets are transmitted to a device through a high-speed link and are forwarded out through a low-speed link.
  Traffic aggregation: Packets are transmitted from multiple interfaces to a device and are forwarded out through a single interface without enough bandwidth.

## Slide 66: Impact of Congestion
Traffic congestion has the following adverse impacts on network traffic:
Traffic congestion intensifies delay and jitter.
Overlong delays lead to packet retransmission.
Traffic congestion lowers the network throughput and damages network resources.
Intensified traffic congestion consumes a large number of network resources (especially storage resources). Unreasonable resource allocation may cause resources to be locked and the system to break down.
Impact
Solution
Congestion avoidance
Congestion management
Notes: Impact of congestion:
  Congestion prevents traffic from obtaining resources immediately, which causes service deterioration. However, congestion often occurs in a complex networking environment where packet transmission and provisioning of various services are both required. Therefore, effective methods are required to avoid congestion or prevent congestion from aggravating.
Solutions:
  The solutions need to make full use of network resources on the premise of meeting users' requirements for service quality. Congestion management and congestion avoidance are commonly used to relieve traffic congestion.
  Congestion management provides means to manage and control traffic when traffic congestion occurs.
  Congestion avoidance is a flow control technique used to relieve network overload. By monitoring the usage of network resources in queues or memory buffer, a device automatically drops packets on the interface that shows a sign of traffic congestion. Congestion avoidance prevents queues from being overflowed due to network overload. The following will introduce congestion avoidance technology.

## Slide 67: Congestion Avoidance Technology
Congestion avoidance is a flow control technique used to relieve network overload. By monitoring the usage of network resources for queues or memory buffers, a device automatically drops packets that shows a sign of traffic congestion.
Queue 0
Queue 1
Queue 2
Queue N
…
Congestion avoidance
Enter a queue
Monitor
Data sending queue
If congestion becomes severe, the packets that do not enter queues are discarded.
Tail drop: traditional processing
Random Early Detection (RED)
Weighted Random Early Detection (WRED)
Drop policies

## Slide 68: Policy 1: Tail Drop
When the length of a queue reaches the maximum value, the device enabled with tail drop discards all new packets buffered at the tail of the queue.
Six packets per second
Four packets per second
4 | 3 | 2 | 1
6 | 5
The queue is full.
Subsequent packets sent to the queue are directly discarded.
Notes: Due to the limited length of each queue, when a queue is full, the traditional processing method discards all the packets sent to the queue until the congestion is relieved. This processing method is called tail drop.

## Slide 69: Disadvantage 1: Global TCP Synchronization
When the length of a queue reaches the maximum value, the device enabled with tail drop discards all new packets buffered at the tail of the queue.
Problem
Global TCP synchronization
The TCP connection cannot be established.
Process:
TCP starts.
Traffic is too heavy. As a result, the queue is full and tail drop occurs.
The TCP ACK packet returned by the server is discarded due to congestion. Therefore, the sender does not receive the TCP ACK packet and considers that the network is congested. In this case, the TCP sliding window size is reduced, and the overall traffic is also reduced.
At this time, network congestion is eliminated, and the sender can receive the TCP ACK packet. Therefore, the sender considers that the network is not congested, and enters the TCP slow start process. This process is repeated.
Traffic
Time
Maximum value
1
2
3
4
Notes: As shown in the following figure, three colors indicate three TCP connections.
Global TCP synchronization:
  In tail drop mechanism, all newly arrived packets are dropped when congestion occurs, causing all TCP sessions to simultaneously enter the slow start state and the packet transmission to slow down.
  When packets of multiple TCP connections are discarded in a queue, TCP connections enter the congestion avoidance and slow start state to adjust and reduce traffic. This is called TCP global synchronization. Then all TCP sessions restart their transmission at roughly the same time and then congestion occurs again, causing another burst of packet drops, and all TCP sessions enter the slow start state again. The behavior cycles constantly, severely reducing the network resource usage.

## Slide 70: Disadvantage 2: Undifferentiated Drop
When the length of a queue reaches the maximum value, the device enabled with tail drop discards all new packets buffered at the tail of the queue.
Problem
Undifferentiated drop
Non-key data 4 | Non-key data 3 | Non-key data 2 | Key data 1
The queue is full.
All subsequent packets sent to the queue
will be discarded.
Tail drop may cause a large amount of non-key data to be forwarded and a large amount of key data to be discarded.
Tail drop cannot differentiate traffic.
Cause:
Key data 7 | Key data 6 | Key data 5
Notes: Tail drop cannot differentiate services and discard traffic in the same way.

## Slide 71: Policy 2: RED
Random early detection (RED) randomly discards data packets.
Process:
When the queue length is less than the lower threshold, no packets are discarded.
When the queue length is between the upper threshold and the lower threshold, newly arrived packets are randomly discarded. The longer the queue is, the higher the drop probability is.
All coming packets are discarded if the queue length is greater than the upper threshold.
Drop probability
Actual
queue length
100%
Maximum
drop probability
Lower threshold
Upper threshold
Maximum queue length
Drop probability curve
No drop
Random drop
Tail drop
1
2
3
Notes: RED defines upper and lower thresholds for the length of each queue:
  When the queue length is less than the lower threshold, no packets are discarded.
  When the queue length is greater than the upper drop threshold, all packets are discarded.
  Coming packets are dropped randomly if the queue length is between upper and lower thresholds. RED generates a random number for each incoming packet and compares it with the drop probability of the current queue. If the random number is greater than the drop probability, the packet is discarded. A longer queue indicates a higher drop probability.

## Slide 72: Relieving Global TCP Synchronization
RED randomly discards packets so that rates of TCP connections are reduced at different times. This prevents global TCP synchronization.
Traffic
Time
Maximum value
Disadvantage:
  RED cannot distinguish traffic.
Symptom:
  Global TCP synchronization may still occur, but the link usage is greatly increased.
Global TCP synchronization
Notes: RED is used to avoid global TCP synchronization that occurs with tail drop. It does this by randomly discarding packets so that the transmission speed of multiple TCP connections is not reduced simultaneously. This results in more stable rates of TCP traffic and other network traffic. — Do not adjust TCP sliding window sizes simultaneously.

## Slide 73: Policy 3: WRED
Weighted Random Early Detection (WRED) sets different drop policies for data packets or queues with different priorities to discard different types of traffic.
Example:
The lower threshold is 20 and the upper threshold is 40 for the traffic whose IP precedence is 0.
The lower threshold is 35 and the upper threshold is 40 for the traffic whose IP precedence is 2. The traffic whose IP precedence is 2 is discarded later than the traffic whose IP precedence is 0.
Advantage:
Do not adjust TCP sliding window sizes simultaneously to avoid global TCP synchronization.
Different traffic is discarded based on weights.
Drop probability (%)
Actual
queue length
100%
Maximum
drop probability
20
30
40
35
IP precedence used as an example:
The corresponding precedences are as follows:
0
1
2
Traffic 1
Traffic 2
Traffic 3
1
2
Notes: The device provides WRED based on RED technology.
WRED discards packets in queues based on DSCP priorities or IP priorities. The upper and lower thresholds, and drop probability can be set for each priority. When the number of packets of a priority reaches the lower threshold, the device starts to discard packets. When the number of packets reaches the upper threshold, the device discards all the packets. As the queue length increases, the packet loss rate increases. The maximum packet loss rate does not exceed the preset packet loss rate. WRED discards packets in queues based on the drop probability, thereby preventing congestion to a certain degree. — Do not adjust TCP sliding window sizes simultaneously.

## Slide 74: WRED Drop Priority
Service class
Color
Uplink direction
Drop priority
of packets
on the device
Color
VLAN packet
MPLS packet
IP packet
Green
Yellow
Red
Priority in descending order
Service class
Color
Mapping
SFU
Downlink direction
802.1p
MPLS EXP
DSCP
Mapping
802.1p
MPLS EXP
DSCP
Color/Drop Probability |  |  | 
Example: AF | AF41 | AF42 | AF43
Lower threshold | 70 | 50 | 30
Upper threshold | 80 | 60 | 40
Drop probability | 70% | 80% | 90%
Service Class/Color |  |  | 
AF | AF41 | AF42 | AF43
 | AF31 | AF32 | AF33
 | AF21 | AF22 | AF23
 | AF11 | AF12 | AF13
Notes: Color：
  The color of packets determines the order in which packets are dropped in a congested queue.
Application:
  The WRED lower threshold is recommended to start from 50% and change with the drop priority. The lowest drop probability and highest lower and upper thresholds are recommended for green packets; a medium drop probability and medium lower and upper thresholds are recommended for yellow packets; the highest drop probability and smallest lower and upper thresholds are recommended for red packets.
  When traffic congestion aggravates, red packets are first dropped due to the smallest lower threshold and high drop probability. As the queue length increases, the device drops green packets at last. If the queue length reaches the upper threshold for red/yellow/green packets, red/yellow/green packets start to be tail dropped.

## Slide 75: Curve of the WRED Drop Probability
Color/Drop Probability |  |  | 
Example: AF | AF41 | AF42 | AF43
Lower threshold | 70 | 50 | 30
Upper threshold | 80 | 60 | 40
Drop probability | 70% | 80% | 90%
Drop probability
Actual
queue length
100%
Red packet discard probability
Red
Lower threshold
Red
Upper threshold
Yellow
Upper threshold
Yellow
Upper threshold
Green
Upper threshold
Green
Upper threshold
Maximum
queue length
Yellow packet discard probability
Green packet discard probability
Differentiated drop for different traffic
Notes: Color：
  The color of packets determines the order in which packets are dropped in a congested queue.
Application:
  The WRED lower threshold is recommended to start from 50% and change with the drop priority. The lowest drop probability and highest lower and upper thresholds are recommended for green packets; a medium drop probability and medium lower and upper thresholds are recommended for yellow packets; the highest drop probability and smallest lower and upper thresholds are recommended for red packets.
  When traffic congestion aggravates, red packets are first dropped due to the smallest lower threshold and high drop probability. As the queue length increases, the device drops green packets at last. If the queue length reaches the upper threshold for red/yellow/green packets, red/yellow/green packets start to be tail dropped.

## Slide 76: Application of Congestion Avoidance
Video flow
Voice flow
Data flow
Video
Voice
Data
LAN
WAN
LAN
Traffic direction
Configure congestion avoidance
in the outbound direction of the interface
Notes: Example:
  Users in different LANs may upload data to the same server, so data exchanged between users and the server passes the WAN. Because WAN bandwidth is lower than LAN bandwidth, congestion may occur on the edge device between the WAN and LANs. Congestion avoidance can be configured on the edge device to discard low-priority packets such as data packets, reducing network overload and ensuring forwarding of high-priority services.

## Slide 77: Configuring Queue-based WRED
The device supports WRED based on DSCP priorities or IP priorities. The configuration roadmap is as follows:
  Configure a drop profile.
  Configure WRED parameters.
  Reference the drop profile to a queue profile.
  Apply the queue profile to the outbound direction of the interface.
system-view
drop-profile [drop-profile-name] //Create a drop profile.
wred [dscp | ip-precedence] //Configure a WRED drop profile based on DSCP or IP priorities.
dscp [dscp-value] low-limit [low-limit-percentage] high-limit [high-limit-percentage] discard-percentage [discard-percentage] //Configure WRED parameters based on DSCP priorities.
ip-precedence [ip-precedence-value] low-limit [low-limit-percentage] high-limit [high-limit-percentage] discard-percentage [discard-percentage] //(Optional) Configure WRED parameters based on IP priorities.
qos queue-profile [queue-profile-name] //Enter the queue profile view.
queue [queue-index] drop-profile [drop-profile-name] //Bind the drop profile to the specified queue in the queue profile.
interface [interface-type interface-num] //Enter the interface view.
qos queue-profile [queue-profile-name] //Apply the queue profile to the interface.
DS edge device
DS node
DS domain

## Slide 78: Configuring MQC to Implement Congestion Avoidance (1)
After a drop profile is bound to a traffic behavior, associate the traffic behavior with the corresponding traffic classifier in the traffic policy and apply the traffic policy to an interface to implement congestion avoidance for traffic matching the traffic classifier. The configuration roadmap is as follows:
  Configure a drop profile.
  Configure a traffic classifier and a traffic behavior.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to the outbound direction of the device interface.
system-view
drop-profile [drop-profile-name] //Create a drop profile.
wred [dscp | ip-precedence] //Configure a WRED drop profile based on DSCP or IP priorities.
dscp [dscp-value] low-limit [low-limit-percentage] high-limit [high-limit-percentage] discard-percentage [discard-percentage] //Configure WRED parameters based on DSCP priorities.
ip-precedence [ip-precedence-value] low-limit [low-limit-percentage] high-limit [high-limit-percentage] discard-percentage [discard-percentage] //(Optional) Configure WRED parameters based on IP priorities.
DS edge device
DS node
DS domain

## Slide 79: Configuring MQC to Implement Congestion Avoidance (2)
After a drop profile is bound to a traffic behavior, associate the traffic behavior with the corresponding traffic classifier in the traffic policy and apply the traffic policy to an interface to implement congestion avoidance for traffic matching the traffic classifier. The configuration roadmap is as follows:
  Configure a drop profile.
  Configure a traffic classifier and a traffic behavior.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to the outbound direction of the device interface.
DS edge device
DS node
DS domain
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on traffic characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
drop-profile [drop-profile-name] //Bind the created drop profile to the traffic behavior.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] outbound //Apply the traffic policy to the outbound direction of the interface.

## Slide 80: Checking the Congestion Avoidance Configuration
Checking the queue-based congestion avoidance configuration
Checking the MQC-based congestion avoidance configuration
system-view
interface [interface-type interface-num]
display this //Check the queue profile bound to the interface.
qos queue-profile [queue-profile-name]
display this //Check the drop profile bound to the queue profile.
display drop-profile [ drop-profile-name ] //Check the drop profile configuration.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.

## Slide 81
(Multiple-answer question) Which of the following mechanisms are used by QoS to proactively discard packets?( )
  Tail drop
  RED
  MRED
  WRED
Notes: ABD

## Slide 82
Congestion avoidance technology cannot avoid congestion, but prevents problems caused by congestion. For example, tail drop causes global TCP synchronization, interface traffic is unstable, and UDP traffic preempts the bandwidth used by TCP traffic.
RED/WRED randomly discards data packets to prevent problems such as global TCP synchronization.

## Slide 83
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 84: QoS Data Processing
Traffic classification
CAR
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Enter a queue
Scheduling
Outbound interface
Leave a queue
Video
Voice
Data
Inbound interface
Token
Token bucket
Congestion management
Notes: Congestion management: It is a measure that must be taken to solve the problem of resource competition. Packets are buffered in queues and a scheduling algorithm is used to determine the forwarding sequence of packets. Congestion management is usually applied to the outbound direction of an interface.

## Slide 85: Congestion Management Technology
Congestion management technology manages and controls different types of service traffic when network congestion occurs.
It uses queue scheduling technology to handle traffic congestion.
Queue 0
Queue 1
Queue 2
Queue N
…
Scheduling
Leave a queue
Data sending queue
Packets are scheduled based on the priority of each queue.
Congestion management
Notes: Congestion Management Technology
Congestion management defines a policy that determines the order in which packets are forwarded and specifies drop principles for packets. The queuing technology is used.
The queue scheduling algorithm determines the order in which packets are leaving a queue and the relationships between queues.
Queuing technology
Packets sent from one interface are placed into many queues which are identified with different priorities. The packets are then sent based on the priorities. Different queue scheduling mechanisms are designed for different situations and lead to varying results.

## Slide 86: What Is a Queue?
The queuing technology orders packets in the buffer.
Each interface has eight downlink queues, which are called class queues (CQs) or port queues.
They are EF, AF1, AF2, AF3, AF4, BE, CS6, and CS7.
Queue
Notes: What is a queue?
  The queuing technology orders packets in the buffer. When the packet rate exceeds the interface bandwidth or the bandwidth configured for packets, the packets are buffered in queues and wait to be forwarded.
  Each interface on the NE20E or NE40E stores eight downlink queues, which are called CQs or port queues. The eight queues are BE, AF1, AF2, AF3, AF4, EF, CS6, and CS7.

## Slide 87: Queue Scheduling Algorithms
Congestion management uses the queuing technology.
First In First Out (FIFO)
Strict Priority (SP)
Weighted Fair Queuing (WFQ)
Queue scheduling algorithms
Notes: Queuing technology places packets sent from one interface into multiple queues with different priorities. These packets are then sent based on the priorities. Different queue scheduling mechanisms are designed for different situations and lead to varying results.

## Slide 88: FIFO
The FIFO mechanism is used to transfer packets in a queue. Resources used to forward packets are allocated based on the arrival order of packets.
Packet 1
Packet 2
Packet 3
FIFO
Scheduling
Queue
FIFO
Enter a queue
FIFO
Leave a queue
Packet 1
Packet 2
Packet 3
Notes: FIFO does not classify packets.
FIFO allows the packets that come earlier to enter the queue first. On the exit of a queue, FIFO allows the packets to leave the queue in the same order as that in which the packets enter the queue.
Characteristics:
  Advantage: The implementation mechanism is simple and the processing speed is fast.
  Disadvantage: Packets with different priorities cannot be processed in differentiated ways.

## Slide 89: SP
SP schedules packets strictly based on queue priorities.
SP
Scheduling
Leave a queue
High-priority queue
Medium-priority queue
Low-priority queue
Packet 1
Packet 2
Packet 3
Packet 6
Packet 4
Packet 5
Packet 2
Packet 6
Packet 3
Packet 4
Packet 5
Packet 1
Packet 1
Packet 2
Packet 3
Packet 4
Packet 5
Packet 6
Classification
Enter a queue
Notes: SP: Packets in queues with a low priority can be scheduled only after all packets in queues with a higher priority are scheduled.
As shown in the figure, three queues with a high, medium, and low priorities respectively are configured with SP scheduling. The number indicates the order in which packets arrive.
When packets leave queues, the device forwards the packets in descending order of priority. Packets in the higher-priority queue are forwarded preferentially. If packets in the higher-priority queue come in between packets in the lower-priority queue that is being scheduled, the packets in the high-priority queue are still scheduled preferentially. This implementation ensures that packets in the higher-priority queue are always forwarded preferentially. As long as there are packets in the high-priority queue, no other queue will be served.
Characteristics:
  Advantage: High-priority packets are preferentially forwarded.
  Disadvantage: Low-priority queues may be starved out. That is, when congestion occurs, packets in lower-priority queues are not processed until all the higher-priority queues are empty. As a result, a congested higher-priority queue causes all lower-priority queues to starve out.

## Slide 90: WFQ
WFQ allocates outbound bandwidth to flows on an interface based on weights of queues.
8-bit packet
WFQ
Scheduling
Leave a queue
High-priority queue: 50%
Medium-priority queue: 25%
Low-priority queue: 25%
4-bit packet
6-bit packet
Classification
Enter a queue
Bit-by-bit
4-bit packet
6-bit packet
8-bit packet
Packet assembly
Leaving packet
Packet 1
Packet 2
Packet 3
Packet 4
Packet 5
Packet 6
Notes: WFQ allocates bandwidths to flows based on weights of queues. In addition, to fairly allocate bandwidths to flows, WFQ schedules packets bit by bit.
When packets leave queues, the device forwards the packets in descending order of priority. Packets in the higher-priority queue are forwarded preferentially. If packets in the higher-priority queue come in between packets in the lower-priority queue that is being scheduled, the packets in the high-priority queue are still scheduled preferentially. This implementation ensures that packets in the higher-priority queue are always forwarded preferentially. As long as there are packets in the high-priority queue, no other queue will be served.
Characteristics:
  Advantages:
    Packets in different queues are scheduled fairly, and the flow delays have slight differences.
    If many large and small packets in different queues need to be sent, small packets are scheduled first, reducing the total jitter of each flow.
    The smaller the weight, the less the allocated bandwidth. Flows with larger weights are allocated higher bandwidth.
  Disadvantage: Low-latency services cannot be scheduled in a timely manner. User-defined classification rules cannot be implemented.

## Slide 91
Notes: The bit-by-bit scheduling mode, however, is an ideal one. The NE40E performs WFQ scheduling based on a certain granularity, such as 256 bytes and 1 Kbytes. Different cards support different granularities.

## Slide 92: Queue Scheduling Mode of an Interface
You can configure SP scheduling or WFQ scheduling for eight queues on an interface.
Eight queues can be classified into three groups, priority queuing (PQ) queues, WFQ queues, and low priority queuing (LPQ) queues, based on scheduling algorithms.
PQ queue: uses the SP scheduling algorithm.
WFQ queue: uses the WFQ scheduling algorithm.
LPQ queue: uses the SP scheduling algorithm.
Eight interface queues
are classified into three groups
Notes: PQ queue
  SP scheduling applies to PQ queues. Packets in high-priority queues are scheduled preferentially. Therefore, services that are sensitive to delays (such as VoIP) can be configured with high priorities.
  In PQ queues, however, if the bandwidth of high-priority packets is not restricted, low-priority packets cannot obtain bandwidth and are starved out.
  Generally, services that are sensitive to delays are put into PQ queues.
WFQ queue
  WFQ queues are scheduled based on weights. The WFQ scheduling algorithm can be used to allocate the remaining bandwidth based on weights.
LPQ queue
  LPQ is a queue scheduling mechanism that is implemented on a high-speed interface (such as an Ethernet interface). LPQ is not supported on a low-speed interface (such as a serial interface or MP-group interface).
  SP scheduling applies to LPQ queues. The difference is that when congestion occurs, the PQ queue can preempt the bandwidth of the WFQ queue whereas the LPQ queue cannot. After packets in the PQ and WFQ queues are all scheduled, the remaining bandwidth can be assigned to packets in the LPQ queue.

## Slide 93
Notes:   In practice, BE flows can be put into LPQ queues. When the network is overloaded, BE flows can be limited so that other services can be processed preferentially.
WFQ, PQ, and LPQ can be used separately or jointly for eight queues on an interface.

## Slide 94: Scheduling Order of Three Types of Queues
PQ
queue
Queue 1
Queue m
… …
WFQ
queue
Queue 1
Queue i
…
LPQ
queue
Queue 1
Queue k
…
WFQ
scheduling
SP
scheduling
SP
scheduling
SP
scheduling
Destination
interface
Start
Is the PQ queue empty?
Is the WFQ queue empty?
Is the LPQ queue empty?
Perform a round of
PQ scheduling
Perform a round of
WFQ scheduling
Perform a round of
LPQ scheduling
Yes
Yes
Yes
No
No
No
Interface queue scheduling order
Interface queue scheduling process
Notes: Interface queue scheduling order:
  If PQ, WFQ, and LPQ queues use SP scheduling. PQ, WFQ, and LPQ queues are scheduled in sequence.
Interface queue scheduling process:
  Packets in PQ queues are preferentially scheduled, and packets in WFQ queues are scheduled only when no packets are buffered in PQ queues. When all PQ queues are empty, WFQ queues start to be scheduled. Packets in PQ queues are preferentially scheduled,
  and packets in WFQ queues are scheduled only when no packets are buffered in PQ queues. Bandwidths are preferentially allocated to PQ queues to guarantee the PIR of packets in PQ queues.
  Packets in LPQ queues are scheduled only after all packets in WFQ queues are sent.
Scheduling result:
  The PIR of PQ queues is guaranteed first, and the remaining bandwidth is allocated among WFQ queues based on weights.
  When the PIR of all WFQ queues is guaranteed, the remaining bandwidth is allocated to LPQ queues.

## Slide 95: Application of Congestion Management
Video flow
Voice flow
Data flow
Video
Voice
Data
Traffic direction
Configure congestion management
in the outbound direction of the interface
Notes: Example:
  On a network, when multiple services compete for the same resources (such as the bandwidth and buffer), traffic congestion may occur and high-priority services may be not processed in a timely manner. Packets can be sent to different queues according to the priority mapping result, as shown in the figure. Different scheduling modes are set in the outbound direction to implement differentiated services.

## Slide 96: QoS Processing Review
Video
Voice
Data
Inbound interface
Traffic classification
Token bucket
Token
Re-marking
Other
processing
…
Queue 0
Queue 1
Queue 2
Queue N
…
GTS
WRED
Congestion avoidance
Enter a queue
Scheduling
Congestion management
Traffic shaping
Traffic policing
Outbound interface
Leave a queue
CAR

## Slide 97: Configuring Queue-based Congestion Management
WAN interfaces support three scheduling modes: PQ, WFQ, and PQ+WFQ. The configuration roadmap is as follows:
  Create a queue profile.
  Configure scheduling modes.
  Apply the queue profile to the interface.
system-view
qos queue-profile [queue-profile-name] //Create a queue profile.
schedule pq [queue-index] | wfq [queue-index] //Configure scheduling modes for queues on a WAN interface.
interface [interface-type interface-num] //Enter the interface view.
qos queue-profile [queue-profile-name] //Apply the queue profile to the interface.
DS edge device
DS node
DS domain

## Slide 98: Configuring MQC to Implement Congestion Management (1)
MQC provides three types of queues:
  Assured Forwarding (AF) queues
  Expedited Forwarding (EF) or LLQ queues
  BE queues
The configuration roadmap is as follows:
  Configure a traffic classifier and a traffic behavior.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to the outbound direction of the device interface.
DS edge device
DS node
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on traffic characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
queue af bandwidth [bandwidth | pct percentage] //Configure the minimum bandwidth for AF queues in the traffic behavior.
queue ef bandwidth [bandwidth | pct percentage] //Configure the minimum bandwidth for EF queues in the traffic behavior.
queue llq bandwidth [bandwidth | pct percentage] //Configure the maximum bandwidth for LLQ queues in the traffic behavior.
queue wfq queue-number [total-queue-number] //Configure WFQ scheduling parameters for BE queues in the traffic behavior.
DS domain
Notes: AF queue: AF queues ensure that service traffic is forwarded when the traffic rate does not exceed the minimum bandwidth.
EF/LLQ queue: After packets matching certain rules enter EF or LLQ queues, they are scheduled in SP mode. Packets in other queues are scheduled only after all the packets in EF or LLQ queues are scheduled. In addition, EF queues can use the available bandwidth in AF or BE queues. The latency of LLQ queues is lower than that of common EF queues.
BE queue: The remaining packets that do not enter AF or EF queues enter BE queues. BE queues are scheduled using the WFQ algorithm.
The total bandwidth used by AF queues and EF queues cannot exceed 100% of the interface bandwidth.
EF queues are provided with bandwidth preferentially. AF queues share the remaining bandwidth based on their weights.

## Slide 99: Configuring MQC to Implement Congestion Management (2)
MQC provides three types of queues:
  AF queues
  EF/LLQ queues
  BE queues
The configuration roadmap is as follows:
  Configure a traffic classifier and a traffic behavior.
  Bind the traffic classifier and traffic behavior to a traffic policy.
  Apply the traffic policy to the outbound direction of the device interface.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] outbound //Apply the traffic policy to the outbound direction of the interface.
DS edge device
DS node
DS domain
Notes: AF queue: AF queues ensure that service traffic is forwarded when the traffic rate does not exceed the minimum bandwidth.
EF/LLQ queue: After packets matching certain rules enter EF or LLQ queues, they are scheduled in SP mode. Packets in other queues are scheduled only after all the packets in EF or LLQ queues are scheduled. In addition, EF queues can use the available bandwidth in AF or BE queues. The latency of LLQ queues is lower than that of common EF queues.
BE queue: The remaining packets that do not enter AF or EF queues enter BE queues. BE queues are scheduled using the WFQ algorithm.
The total bandwidth used by AF queues and EF queues cannot exceed 100% of the interface bandwidth.
EF queues are provided with bandwidth preferentially. AF queues share the remaining bandwidth based on their weights.

## Slide 100: Checking the Congestion Management Configuration
Checking the queue-based congestion management configuration
Checking the traffic classifier-based congestion management configuration
system-view
interface [interface-type interface-num]
display this //Check the queue profile bound to the interface.
display qos queue-profile [queue-profile-name] //Check the queue profile configuration.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.

## Slide 101
(Single-answer question) How many queues are there on an interface?( )
  6
  7
  8
  9
(Multiple-answer question) Which of the following is a queue scheduling technology?( )
  PQ
  WFQ
  WRED
  FIFO
Notes: C
ABD

## Slide 102
After a data packet enters a queue, the device sends the data packet according to the queue scheduling mechanism.
Common queue scheduling technologies include FIFO, PQ, and WFQ.
PQ scheduling is performed before WFQ scheduling and FIFO. Queues scheduled in WFQ mode can transmit data only when queues scheduled in PQ mode have no data to transmit. The queue scheduled in FIFO mode can transmit data only when queues scheduled in PQ and WFQ mode have no data to transmit.

## Slide 103
Introduction to QoS
Traffic Classification and Marking
Traffic Limiting Technology
Congestion Avoidance Technology
Congestion Management Technology
Introduction to HQoS

## Slide 104: Limitations of QoS
Traditional QoS distributes a flow into only eight queues for scheduling and control. Therefore, it has great limitations in multi-tenant scenarios.
In home broadband scenarios, different families may rent different network bandwidths and network services. Therefore, QoS cannot manage these families in a refined manner.
QoS limitations in home broadband scenarios
Internet
Three tenants subscribe to 20 Mbit/s bandwidth to lease Internet access services.
Three tenants subscribe to 30 Mbit/s bandwidth to lease IPTV services.
Two tenants subscribe to 50 Mbit/s bandwidth to lease VoIP services.
Three tenants subscribe to 20 Mbit/s bandwidth to lease IPTV services.
Three tenants subscribe to 50 Mbit/s bandwidth to lease VoIP services.
User-based QoS cannot be implemented on the egress. Only eight queues can be used to differentiate traffic.
14 households rent different bandwidths and services.

## Slide 105: HQoS Overview
Traditional QoS schedules traffic based on interfaces. An interface can only differentiate service priorities. The traffic of the same priority uses the same interface queue and competes for the same queue resources. Therefore, traditional QoS technology cannot provide differentiated services based on types of traffic and users.
HQoS meets this requirement by implementing hierarchical scheduling based on multiple levels of queues, differentiating both services and users to provide refined QoS guarantee.
Different devices provide different HQoS features. This section describes HQoS features supported by the CPE (AR series router).

## Slide 106: Introduction to HQoS Queues
The CPE supports three-level queues: flow queue (level 3), subscriber queue (level 2), and port queue (level 1).
…
…
…
…
Level 2 subscriber queue
Level 1 port queue
Physical interface
Level 3 flow queue
Level 3 flow queue
Voice flow
Video flow
Tenant 1
Internet access traffic
Gaming flow
Tenant 2
…
Tenant N
Video flow
Other traffic
Sub-interface and tunnel interface
Notes: Flow queue
  The same type of services of a user is taken as a service flow. HQoS schedules queues based on service flows. Flow queues correspond to service types and are classified into EF, AF, and BE queues. You can set scheduling modes for flow queues.
Subscriber queue
  Services from a user are placed into a subscriber queue. HQoS allows all services in the subscriber queue to share the bandwidth.
Port queue
  Each port corresponds to a queue and port queues are scheduled in RR mode. You can configure only interface-based traffic shaping, but cannot configure scheduling modes.

## Slide 107: Introduction to HQoS Queue Scheduling
The flow queue and subscriber queue support PQ scheduling, WFQ scheduling, and PQ+WFQ scheduling. The port queue uses RR scheduling.
HQoS queue scheduling
…
…
…
...
...
PQ/WFQ
PQ/WFQ
PQ/WFQ
RR
Level 3 flow queue
Level 2 subscriber queue
Level 1 port queue
Notes: HQoS deployment for enterprise users is used as an example. Enterprise users have VoIP, video conference, and data services. Each subscriber queue corresponds to one enterprise user and each flow queue corresponds to a type of services. By deploying HQoS, the device can control the following items:
  Traffic scheduling among three types of services of a single enterprise user
  Total bandwidth of three types of services of a single enterprise user
  Bandwidth allocation between multiple enterprise users
  Total bandwidth of multiple enterprise users

## Slide 108: Introduction to HQoS Traffic Shaping
The HQoS shaper buffers packets and limits the rate of packets. The device supports three levels of shapers, that is, flow queue shaper, subscriber queue shaper, and port queue shaper. After packets enter the device, the device buffers the packets in queues and sends the packets at the limited rate. Shapers can ensure the CIR and limit the maximum rate of packets by using the rate limiting algorithm.
Level 1 port queue shaping
Level 2 subscriber queue shaping
Level 3 flow queue shaping
…
Data is buffered in a flow queue and waits to be sent.
Data from multiple flow queues is buffered in a subscriber queue and waits to be sent.
Data from multiple subscriber queues is buffered in a port queue and waits to be sent.

## Slide 109: Introduction to the HQoS Dropper
The HQoS dropper discards packets based on a drop policy before packets are sent to queues.
The three types of queues supported by HQoS support different drop modes. The port queue and subscriber queue support tail drop; the flow queue supports tail drop and WRED.
Level 1 port queue
Level 2 subscriber queue
Level 3 flow queue
…
WRED or tail drop
Tail drop
Tail drop
Discard packets based on drop policies
Discard packets based on drop policies
Discard packets based on drop policies

## Slide 110: HQoS Application Example
Assume that there are three families in a building. Family A purchases 10 Mbit/s bandwidth and enables the VoIP, IPTV, and High Speed Internet (HSI) services. Family B purchases 20 Mbit/s bandwidth and enables the IPTV and HSI services. Family C purchases 30 Mbit/s bandwidth and enables only the HSI service. HQoS can meet these requirements.
Total bandwidth of the building (60 Mbit/s)
Total bandwidth of family A (10 Mbit/s)
Total bandwidth of family B (20 Mbit/s)
Family A
Family B
Family C
Deploy HQoS at the egress
HQoS deployment solution
WFQ
Level 3 flow queue
Level 2 subscriber queue
Level 1 port queue
Total bandwidth of family C (30 Mbit/s)
VoIP (PQ scheduling)
IPTV (PQ scheduling)
HSI (WFQ scheduling)
IPTV (PQ scheduling)
HSI (WFQ scheduling)
HSI (WFQ scheduling)

## Slide 111: HQoS Configuration Roadmap
The HQoS configuration is complex. Generally, the MQC mode is used.
When HQoS is configured, the policy nesting mode is used.
  The parent traffic policy differentiates users, and the child traffic policy differentiates traffic.
  A parent traffic policy can have multiple child traffic policies.
  A parent traffic policy applies to an interface.
Level 1 port queue
Level 2 subscriber queue
Level 3 flow queue
…
Child traffic policy
Parent traffic policy
Interface or sub-interface queue

## Slide 112: Configuring a Child Traffic Policy
Internet
Child traffic policies are used to differentiate services. You can configure multiple child traffic policies based on services when configuring HQoS.
The configuration of HQoS child traffic policies is the same as that of common MQC. The configuration roadmap is as follows:
  Configure a traffic classifier where traffic is matched based on service characteristics.
  Configure a traffic behavior where the queue scheduling mode and queue bandwidth are defined.
  Bind the traffic classifier and traffic behavior to a traffic policy.
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on service characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
queue [af | ef | llq] bandwidth [bandwidth | pct percentage] //Configure AF, EF, or LLQ queue parameters in the traffic behavior.
drop-profile [drop-profile-name] //Bind the created drop profile to the traffic behavior.
system-view
traffic policy [policy-name] //Create a traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.

## Slide 113: Configuring a Parent Traffic Policy
A parent traffic policy is used to differentiate users. When configuring HQoS, you can bind multiple child traffic policies to a parent traffic policy.
The configuration roadmap is as follows:
  Configure a traffic classifier to match traffic based on user characteristics.
  Configure a traffic behavior that needs to invoke a child traffic policy.
  Bind the traffic classifier and traffic behavior to a traffic policy.
system-view
traffic classifier [classifier-name] //Create a traffic classifier.
if-match [acl | vlan-id | …. ] //Match traffic based on user characteristics.
system-view
traffic behavior [behavior-name] //Create a traffic behavior.
queue [af | ef | llq] bandwidth [bandwidth | pct percentage] //(Optional) Configure AF, EF, or LLQ queue parameters in the traffic behavior.
traffic-policy [policy-name] //Bind the sub traffic policy to the traffic behavior.
system-view
traffic policy [policy-name] //Create a parent traffic policy.
classifier [classifier-name] behavior [behavior-name] //Bind the traffic classifier to the traffic behavior.
Internet

## Slide 114: Applying the Parent Traffic Policy
After configuring a parent traffic policy, bind it to an interface or sub-interface.
If the parent traffic policy is bond to a sub-interface, traffic between different sub-interfaces is sent from the physical interface in polling mode.
The configuration roadmap is as follows:
  Apply the parent traffic policy to the outbound direction of the interface.
system-view
interface [interface-type interface-num] //Enter the interface view.
traffic-policy [policy-name] outbound //Apply the parent traffic policy to the outbound direction of the interface.
Internet

## Slide 115: Checking the HQoS Configuration
After configuring HQoS, you can run the following commands to check the configuration.
system-view
display traffic classifier user-defined [ classifier-name ] //Check the traffic classifier configuration.
display traffic behavior [ system-defined | user-defined ] [ behavior-name ] //Check the traffic behavior configuration.
display traffic policy user-defined [ policy-name ] classifier [classifier-name ] //Check the traffic policy configuration.
display traffic-policy applied-record [ policy-name ] //Check the record of the specified traffic policy.

## Slide 116
(True or false) HQoS cannot distinguish users or services.( )
  True
  False
(Multiple-answer question) What are three types of HQoS queues?( )
  Flow queue
  Subscriber queue
  Data queue
  Port queue
Notes: B
ABD

## Slide 117
HQoS can ensure services with finer granularities.
HQoS has three levels of queues: flow queue, subscriber queue, and port queue. Traffic shaping can be deployed for the three types of queues. Flow queues are scheduled in PQ+WFQ mode, subscriber queues are scheduled in PQ+WFQ mode, and interface queues are scheduled in RR mode.

## Slide 118
QoS is an important means to ensure service quality. Generally, the DiffServ model is used on the live network.
This model uses rate limiting, congestion avoidance, and congestion management.
HQoS is used in complex scenarios with finer granularity. Flow queues, subscriber queues, and port queues can be used to distinguish different users and different services of the same user.