## Slide 1
Datacom
Genera
V1.0
hejunjian/hwx580230
2020.03.10
zhushigeng/z00261992
New
hejunjian/hwx580230
2021.07.25
wuyue/wwx291773
Update

## Slide 2: Network Troubleshooting

## Slide 3
Digital transformation of medium- and large-sized enterprises is implemented using multiple technologies, such as cloud computing, big data, artificial intelligence (AI), and Internet of Things (IoT). These technologies are all supported by data communications networks. A stable data communications network requires fully prepared network design, construction, and maintenance.
An enterprise data communications network accommodates various types of devices that are connected by multiple types of physical links. In addition, to accurately forward data packets, the devices run multiple protocols. Network devices, cables, and protocols may encounter faults. How to quickly rectify faults is a basic skill of senior network engineers.
This course describes common network faults, how to troubleshoot them in an effort to help network engineers build capabilities of troubleshooting faults in various scenarios.

## Slide 4
On completion of this course, you will be able to:
  Understand the troubleshooting methods.
  Analyze loop faults.
  Analyze failures to establish neighbor relationships of routing protocols.
  Write a troubleshooting guide.

## Slide 5
Troubleshooting Data Communication Network Faults
  Overview of Network Faults
  Structured Troubleshooting Process
  Core Ideas and Methods of Network Troubleshooting
Troubleshooting Common Network Faults

## Slide 6: What Is a Network Fault?
A network fault refers to the phenomenon that a network loses a specific function and adversely affects services due to some reasons.
From the perspective of users, any phenomenon that adversely affects services can be defined as a fault.
The common fault symptoms and categories are as follows:
Symptom Category | Alarm | Loop | Service Forwarding Failure | Service Interruption | Transient Service Interruption | Packet Loss | Protocol Anomaly | Protocol Flapping | Route Anomaly
Hardware | √ |  |  | √ |  | √ |  |  | 
Configuration |  | √ | √ |  |  |  | √ |  | √
Network |  | √ | √ | √ | √ | √ | √ | √ | √
Performance | √ |  |  |  | √ | √ |  | √ | √
Software |  |  |  |  |  |  | √ |  | √
Interconnection |  | √ | √ |  |  |  | √ |  | 
Others | √ |  | √ | √ | √ | √ |  |  | 
Notes: Mapping between the preceding fault symptoms and categories varies according to scenarios.

## Slide 7
Troubleshooting Data Communication Network Faults
  Overview of Network Faults
  Troubleshooting Process
  Core Ideas and Methods of Network Troubleshooting
Troubleshooting Common Network Faults

## Slide 8: Structured Network Troubleshooting Process
No
Yes
Cause listing
Fault resolving
Fault assessment
Identification and analysis
The network recovers.
Fault confirmation
Is fault rectified?
Information collection
Fault report
Wrap-up work
Step-by-step troubleshooting
Structured network troubleshooting
Notes: If an unstructured network troubleshooting is carried out, steps are performed repeatedly, leading to low efficiency even though a solution to the fault is found.
In a complex network environment, a new fault may be caused due to an unstructured network fault rectification process, making network fault rectification more difficult.

## Slide 9: Fault Report
An enterprise has multiple departments, such as finance, human resource, logistics, marketing, and R&D departments. These departments need to communicate. To properly guarantee network operations, enterprises may take the following measures:
  Large- and medium-sized enterprises set up network maintenance departments to build professional network teams.
  To reduce expenses, small-sized enterprises do not set up an independent network maintenance department. Instead, they entrust their networks to professional network maintenance companies.
  Contact device manufacturers for after-sales service.
Generally, the person who first percepts network faults is from a department related to services, rather than a network maintenance engineer. Network engineers often receive calls for help, such as "the computer suddenly cannot access the Internet", "the web page cannot be displayed normally", and "the game is stuck".
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work
Network O&M area
Cloud/ Data center

## Slide 10: Fault Report: Proactive Communication and Confirmation
Ask a user for the preceding information through a phone and record the information in a troubleshooting report.
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work
Fault reporter | Name, department, position, work content, computer location (floor, room, wireless or wired access), and website that the computer attempts to access.
Fault frequency | Check whether the fault occurs suddenly, occasionally, or frequently.
User operation | Operations performed by a user on a terminal before and after a fault occurs. For example, the IP address and DNS parameters are changed, desktop firewall software is installed, and security control software is installed.
Notes: Why do we need to know the positions and work content of users?
  In an enterprise environment, network access permissions to be granted vary according to positions. Even users of the same position may have only the permission to use network services related to their work content.

## Slide 11: Fault Confirmation
Four factors for determining a fault:
  Subject: network service that becomes faulty
  Symptom: symptom of the fault
  Time: the time when a fault was found and the fault occurrence time estimated by professional personnel
  Location: network component that becomes faulty
Describe the fault symptom accurately.
Ultimately, check whether the fault is within the responsibility scope, that is, whether related permissions have been granted to rectify the fault.
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work
Notes: Why do we need to confirm a fault?
  The user description may be ambiguous, and the reported fault may not be the actual faulty point. In this situation, experienced engineers have to confirm the fault.

## Slide 12: Information Collection
Which information needs to be collected?
  In the information collection phase, fault-related information, such as documents and network changes, is collected.
How to collect the information:
  Run commands on an involved device. Use information collection tools, such as the packet information obtaining tool and network management software.
Obtaining permissions:
  In a network environment that poses high requirements on information security, information collection must be authorized. Sometimes, a written authorization file must be signed.
Risk assessment in the information collection phase:
  Some information collection operations, such as running a debug command on a router or switch, may cause high CPU usage. In worse cases, a device may even stop responding to instructions, causing more faults. When collecting information, you must evaluate risks, balance the risks of introducing new faults and the urgency of rectifying existing faults, and notify users of the risks. Then, users determine whether to collect information in case of high risks.
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 13: Identification and Analysis
In the identification and analysis phase, the collected information is analyzed and sorted.
  By summarizing the fault, maintenance, and version-specific change information and using team (or personal) experience, you can obtain the list of possible causes for network faults.
Team experience
Cause listing
Change information
Maintenance information
Fault information
Identification and analysis
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 14: Cause Listing
In the cause listing phase, you must list all possible fault causes, sort out the most likely causes, and exclude the least possible causes to narrow down the troubleshooting scope.
Possible cause 1
Information filtering
Possible cause 2
Possible cause 3
Possible cause 4
...
Cause 1 to be located
Cause 2 to be located
Causes excluded
Cause listing
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 15: Fault Assessment
Fault assessment must be performed before each check.
Step-by-step troubleshooting
Cause 1 to be located
Fault cause 2 to be located
Root cause
Cause listing
Fault assessment
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work
Notes: A temporary network environment may need to be built for fault evaluation.
  If a complex network fault cannot be rectified within a short period of time after being evaluated and a user wants to immediately restore network availability, you advise the user to temporarily skip the faulty node and build an alternative network environment.
  When building a temporary network environment, fully consider the urgency of solving problems and the risk of bypassing certain security restrictions. Fully communicate with users and implement the environment only after obtaining permissions.

## Slide 16: Step-by-Step Troubleshooting
In the phase of step-by-step troubleshooting, the conflict between the urgency of solving problems and the risk of introducing new faults must be balanced. Therefore, users must be clearly informed of the risks that may be induced the process. Perform the check only after being authorized.
In some cases, network changes may be involved in the verification process. In this case, a complete emergency plan and rollback preparations must be made.
Cause 1 to be located
Cause 2 to be located
Root cause
Step-by-step troubleshooting
Rollback preparations
Emergency plan
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 17: Fault Resolving
After the root cause is found and the fault is rectified, the troubleshooting is complete.
In a complex network environment, you have to observe the network for a period of time after the fault symptom disappears. On the one hand, you can confirm that the fault reported by the user has been rectified. On the other hand, you can confirm that no new fault is introduced during the troubleshooting process.
Continual observation
Wrap-up work
Step-by-step troubleshooting
Root cause
Fault resolving
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 18: Wrap-up Work
Wrap-up work involves arranging related documents and sending notifications. Back up all changed configurations or software in the previous network troubleshooting process, and sort out and hand over troubleshooting documents. To prevent the same fault from occurring again, provide improvement suggestions for users in this phase.
Troubleshooting process documents
Affected parties
Change backup and maintenance suggestions
Troubleshooting summary report
Authorizing party in each phase of troubleshooting
Others: vendors and service providers
Wrap-up work
Document handover
Information notification
Fault Report
Fault Confirmation
Information Collection
Identification and Analysis
Cause Listing
Fault Assessment
Step-by-Step Troubleshooting
Fault Resolving
Wrap-up Work

## Slide 19
Troubleshooting Data Communication Network Faults
  Overview of Network Faults
  Troubleshooting Process
  Core Ideas and Methods of Network Troubleshooting
Troubleshooting Common Network Faults

## Slide 20: Service Traffic Path-Centric Troubleshooting Ideals
The path along which service traffic passes is usually designed in the network planning phase. You merely need to know the round-trip path of service traffic adversely affected by a network fault, trace the path, and rectify the fault step by step.
Network
Service
Finance
OA
Production
Other
services

## Slide 21: Determining a Service Traffic Path: Network Layer
Multiple paths may exist during packet forwarding. Therefore, you need to determine the path over which service traffic is transmitted based on the packet forwarding process.
Path 1
Path 2
IP header | TCP header | Data

## Slide 22: Determining a Service Traffic Path: Data Link Layer
Check how data frames of service traffic are forwarded by switches on a Layer 2 network.
Path 1
Path 2
Ethernet header | IP header | TCP header | Data | FCS

## Slide 23: Layered Troubleshooting Approach
The layered troubleshooting approach is simple, because all working models follow a simple rule: the upper-layer structure of any model can work properly as long as the lower-layer structure is working properly.
Check whether the physical status of an interface is up and whether cables and connectors are securely connected.
Check whether data link layer encapsulation is correct, whether an interface protocol is up, and whether Layer 2 addressing is normal.
Check whether routes are available and whether a routing protocol is working properly.
Check whether TCP connections are correctly established and whether TCP and UDP ports are enabled.
Application layer
Presentation layer
Session layer
Transport layer
Network layer
Data link layer
Physical layer

## Slide 24: Configuration Comparison Approach
Compare configurations, software versions, and hardware models in normal and faulty states to find differences.
Network troubleshooting personnel with less experience will use this method more frequently in practice.
#
sysname r1
#
isis 1
network-entity 49.0001.1000.0000.0001.00
#
interface Serial4/0/0
link-protocol ppp
ip address 10.0.12.1 255.255.255.0
isis enable 1
isis timer hello 30
#
interface LoopBack0
ip address 10.0.1.1 255.255.255.255
isis enable 1
#
#
sysname r1
#
isis 1
network-entity 49.0001.1000.0000.0001.00
#
interface Serial4/0/0
link-protocol ppp
ip address 10.0.12.1 255.255.255.0
isis enable 1
isis timer hello 120
#
interface LoopBack0
ip address 10.0.1.1 255.255.255.255
isis enable 1
#
Compare them

## Slide 25: Block-based Troubleshooting Approach
The configuration files of Huawei network devices, such as switches and routers, are edited in a clear structure.
If a fault occurs, you can narrow down the fault locating scope by classifying the fault into one or several categories:
  Management (router name, password, service, and log)
  Ports (address, encapsulation, cost, and authentication)
  Routing protocols (static route, RIP, OSPF, BGP, and route import)
  Policies (routing policy, policy-based routing, and security configuration)
  Access (console port login, Telnet login, dial-up)
  Applications (DNS, DHCP, and VPN configuration)

## Slide 26: Block-based Troubleshooting Approach: Example
After the display ip routing-table command is run, only direct routes are displayed. What are possible causes?
The fault is related to the following blocks: routing protocols, policies, and ports. If no routing protocol is configured or a routing protocol is incorrectly configured, the routing table may be empty. If an ACL is incorrectly configured, route update may be adversely affected. If the IP address, mask, or authentication configuration of an interface is incorrect, the routing table may be incorrect.
<R2>display ip routing-table Route Flags: R - relay, D - download to fib ------------------------------------------------------------------------------------------------------------------------------------------ Routing Tables: Public Destinations : 16 Routes : 16 |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
10.0.12.1/32 | Direct | 0 | 0 | D | 10.0.12.1 | Serial4/0/0
10.0.12.2/32 | Direct | 0 | 0 | D | 127.0.0.1 | Serial4/0/0
10.0.12.255/32 | Direct | 0 | 0 | D | 127.0.0.1 | Serial4/0/0
10.0.23.0/24 | Direct | 0 | 0 | D | 10.0.23.2 | GigabitEthernet0/0/0
10.0.23.2/32 | Direct | 0 | 0 | D | 127.0.0.1 | GigabitEthernet0/0/0
10.0.23.255/32 | Direct | 0 | 0 | D | 127.0.0.1 | GigabitEthernet0/0/0

## Slide 27: Segment-based Troubleshooting Approach
Since data packets may pass through multiple routers and physical links, each segment may encounter a fault. In this situation, the segment-based approach applies.
Segment 1
Segment 2
Segment 3
Segment 4
PC
Access switch
Aggregation switch
Core switch
Internet

## Slide 28: Replacement Approach
The replacement approach is one of the most common methods for checking hardware problems.
If a network cable may be faulty, replace it with another one in good condition. If an interface module may fail, replace it with another interface module that is working properly.
Replacing a terminal
Replacing a cable
Replacing a device

## Slide 29: Requirements for Network Maintenance and Management Personnel
Have an in-depth understanding of protocol requirements.
Be able to guide a customer to describe the fault symptom and related information in detail.
Fully understand the networks managed and maintained.
Record troubleshooting documents and summarize troubleshooting experience.
Be familiar with network troubleshooting approaches and combine them flexibly.

## Slide 30
(Multiple-answer question) In the wrap-up work of a structured network troubleshooting process, which of the following parties should be notified of information? ( )
  Related parties affected by the fault
  Authorizing parties in each phase of troubleshooting
  Manufacturer and service providers
  Other irrelevant personnel who are interested in the root cause
(True or false) On a large-scale network, the comparison approach is the most effective method for troubleshooting faults. ( )
  True
  False
Notes: ABC
False

## Slide 31
Troubleshooting Data Communication Network Faults
Troubleshooting Common Network Faults
  LAN Faults
  Route Faults
  Service Faults

## Slide 32: Troubleshooting Common Network Faults: Topology (1)
During network maintenance, network engineers may encounter various network faults, such as login, route, and IP service faults. The left figure shows a part of the network architecture, which is used as an example to describe how to troubleshoot common network faults.
Routing protocol overview:
  OSPF: runs between R1 and R2. OSPF is enabled on all interfaces of R1, and GE 0/0/0 belongs to area 0.
  IS-IS: runs between R2 and R3.
  BGP: R1 and R3 establish IBGP peer relationships with R2 and function as clients of R2, namely, the RR.
  Static route: SW3, SW4, and SW5 use static routes to connect to routers.
Static
Static
PC1
PC2
PC13
PC14
PC5
Server6
R1
R2
R3
SW1
SW2
SW3
SW4
SW6
GE0/0/1
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
GE0/0/11
GE0/0/10
GE0/0/11
GE0/0/4
GE0/0/10
GE0/0/11
GE0/0/2
GE0/0/0
OSPF
IS-IS
SW5
IBGP
IBGP

## Slide 33: Troubleshooting Common Network Faults: Topology (2)
IP address planning:
  Loopback0: are 10.0.1.1/32, 10.0.2.2/32, and 10.0.3.3/32 on R1, R2, and R3, respectively.
  Interconnection interfaces: The network segment is shown in the preceding figure, and the decimal number of the right-most octet in an IP address is a device ID.
  Terminals: The network segment is shown in the figure. A gateway has the largest IP address on a network segment. PC5 obtains an IP address using DHCP, and R3 functions as a DHCP server. Other terminals use static IP addresses, with the decimal number of the right-most octet in an IP address indicating a device ID.
Route advertisement planning:
  On R2, configure OSPF and IS-IS to import routes from each other, so that Loopback0 addresses on R1, R2, and R3 are reachable.
  R1 imports static routes destined for 192.168.12.0/24 and 192.168.34.0/24 into the BGP routing table.
  R3 imports the static route destined for 192.168.56.0/24 into the BGP routing table.
MSTP
Instance 12 vlan 12
Instance 34 vlan 34
PC1
PC2
PC13
PC14
PC5
Server6
R1
R2
R3
SW1
SW2
SW3
SW4
SW6
.2
SW5
10.0.23.0/24
.3
.1
.2
10.0.12.0/24
10.0.14..0/24
VLAN 12
192.168.12.0/24
VLAN 34
192.168.34.0/24
VLAN 56
192.168.56.0/24
VLAN 35
10.0.35..0/24
10.0.13..0/24
Notes: R3 and SW5 are connected through Layer 3 sub-interfaces.

## Slide 34: Troubleshooting Common Network Faults: Topology (3)
MSTP planning:
VRRP planning:
The Telnet username and password for login are Huawei and Huawei@123, respectively.
MSTP
Instance 12 vlan 12
Instance 34 vlan 34
PC2
PC13
PC14
PC5
Server6
R1
R2
R3
SW1
SW2
SW3
SW4
SW6
.2
SW5
10.0.23.0/24
.3
.1
.2
10.0.12.0/24
VLAN 13
10.0.13..0/24
VLAN 14
10.0.14..0/24
VLAN 12
192.168.12..0/24
VLAN 34
192.168.34..0/24
VLAN 56
192.168.56..0/24
VLAN 35
10.0.35..0/24
Instance ID | VLAN ID | Root Bridge | Backup Bridge
Instance 12 | VLAN 12 | SW3 | SW4
Instance 34 | VLAN 34 | SW4 | SW3
Network Segment | Master Gateway | Backup Gateway | VRID | Virtual IP
192.168.12.0/24 | SW3 | SW4 | 1 | 192.168.12.254
192.168.34.0/24 | SW4 | SW3 | 2 | 192.168.34.254
PC1

## Slide 35: Common Network Troubleshooting: Symptom
The following symptoms are found:
  PC1 and PC13 cannot communicate.
  Server 6 provides the FTP service, but PC1 cannot use this service.
  PC5 cannot communicate with any host.
There are multiple possible causes. The preceding approaches are used to demonstrate how to troubleshoot the three faults.
Assume that the symptoms have been confirmed. Skip the following steps in the subsequent troubleshooting: fault report, fault confirmation, information collection, and wrap-up work.
MSTP
Instance 12 vlan 12
Instance 34 vlan 34
Static
Static
PC1
PC2
PC13
PC14
PC5
Server6
R1
R2
R3
SW1
SW2
SW3
SW4
SW6
OSPF
IS-IS
SW5
IBGP
IBGP

## Slide 36: PC1 and PC13 Cannot Communicate (1)
Simplified topology:
The figure on the left shows the planned path for PC1-to-PC13 traffic. Use the layered, segment-based, and forwarding path-centric approaches to analyze the faults. PC1 and PC13 fail to communicate due to the following causes:
  Physical link fault
  Incorrectly configured IP address
  VLAN configuration error
  Loop
  VRRP fault
MSTP
PC1
PC13
SW1
SW2
SW3
SW4
Planned traffic path
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Notes: This section describes common troubleshooting methods and tools, providing guidance for network maintenance personnel. The processing sequence in actual scenarios can be different from that in the example.

## Slide 37: PC1 and PC13 Cannot Communicate (2)
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
On PC1 and PC13, choose Control Panel > Network and Internet > Network Connection > Ethernet Cable to check Ethernet cables and ensure that the physical cable connections to the PCs are correct. (The preceding path varies according to an operating system and version.)
Check the physical interface status on each involved switch (SW1, for example). If the physical status of an interface is not up, use another interface to connect the switch to a PC.
PC1
PC13
<SW1>display interface brief ¦ include up |  |  |  |  |  | 
Interface | PHY | Protocol | InUti | OutUti | inErrors | outErrors
GigabitEthernet0/0/3 | up | up | 0% | 0% | 0 | 0
GigabitEthernet0/0/4 | up | up | 0% | 0% | 0 | 0
GigabitEthernet0/0/10 | up | up | 0% | 0% | 0 | 0
GigabitEthernet0/0/11 | up | up | 0% | 0% | 0 | 0
<SW1>display interface GigabitEthernet 0/0/10
Description:
Switch Port, PVID : 12, TPID : 8100(Hex), The Maximum Frame Length is 9216
IP Sending Frames' Format is PKTFMT_ETHNT_2, Hardware address is 4c1f-cc69-6d7b
Hardware address is 4c1f-cc69-6d7b
Last 300 seconds input rate 0 bytes/sec, 0 packets/sec
Last 300 seconds output rate 0 bytes/sec, 0 packets/sec
Input: 430 bytes, 6 packets
Output: 197137 bytes, 1659 packets
Ping 192.168.34.13 from PC1 and check whether the number of packets sent and received by the interface increases. If so, the physical link is working properly. If not, use another interface or replace the network cable.
Notes: This section uses the Windows 10 OS as an example to describe how to check the physical connection status of a PC.
InUti: input bandwidth utilization
OutUti: output bandwidth utilization

## Slide 38: PC1 and PC13 Cannot Communicate (3)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Check that PC1's physical IP address is set to 192.168.12.1 and the gateway address is set to 192.168.12.254.
Check the IP addresses on SW3 and SW4 and ensure that the IP addresses are correctly configured. (A VLANIF interface without an IP address assigned will not go up and cannot implement Layer 3 forwarding.)
PC1
PC13
The preceding information indicates that the IP addresses of the interfaces on SW3 and SW4 have been correctly configured.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
<SW3>display ip interface brief |  |  | 
Interface | IP Address/Mask | Physical | Protocol
MEth0/0/1 | unassigned | down | down
NULL0 | unassigned | up | up(s)
Vlanif1 | unassigned | up | down
Vlanif12 | 192.168.12.3/24 | up | up
Vlanif34 | 192.168.34.3/24 | up | up
<SW4>display ip interface brief |  |  | 
Interface | IP Address/Mask | Physical | Protocol
MEth0/0/1 | unassigned | down | down
NULL0 | unassigned | up | up(s)
Vlanif1 | unassigned | up | down
Vlanif12 | 192.168.12.4/24 | up | up
Vlanif34 | 192.168.34.4/24 | up | up

## Slide 39: PC1 and PC13 Cannot Communicate (4)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Query the switch port and VLAN configuration.
PC1
PC13
According to the preceding information, VLAN configurations of GE 0/0/10 and GE 0/0/11 on SW1 are incorrect. Correct VLAN configuration errors. Repeat the preceding step to verify the configurations on the other three switches.
After the VLAN is correctly configured on the switches, check whether PC1 can communicate with other IP addresses on the same network segment. For example, run the ping 192.168.12.13 command on PC1. The command output shows that packet loss occurs and the delay is long.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
[SW1]display vlan
The total number of vlans is : 3
--------------------------------------------------------------------------------
U: Up; D: Down; TG: Tagged; UT: Untagged;
MP: Vlan-mapping; ST: Vlan-stacking;
#: ProtocolTransparent-vlan; *: Management-vlan;
--------------------------------------------------------------------------------
VID Type Ports
--------------------------------------------------------------------------------
12 common TG:GE0/0/11(U) TG:GE0/0/10(U)
34 common TG:GE0/0/11(U) TG:GE0/0/10(U)
VID Status Property MAC-LRN Statistics Description
--------------------------------------------------------------------------------
12 enable default enable disable VLAN 0012
34 enable default enable disable VLAN 0034
Notes: GE 0/0/10 belongs to VLAN 12 and VLAN 34 and works in tagged mode, indicating that the interface is configured as a trunk interface and the PVID is not 12.

## Slide 40: PC1 and PC13 Cannot Communicate (5)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Check the MSTP status on each switch. All ports on SW4 are in the Forwarding state.
PC1
PC13
<SW4>display current-configuration | begin region-configuration
stp region-configuration
region-name TEST //The correct domain name is test, not TEST.
instance 12 vlan 12
instance 34 vlan 34
active region-configuration
#
MSTP faults may be caused by an incorrect domain name setting, incorrect binding between instances and VLANs, or incorrect binding between ports and VLANs. Check the MSTP configuration on SW4.
Correct the domain name on SW4. Ping 192.168.12.13 from PC1. As a result, packet loss occurs now and then.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
<SW4>display stp brief |  |  |  | 
MSTID | Port | Role | STP | State
0 | GigabitEthernet0/0/2 | DESI | FORWARDING | NONE
0 | GigabitEthernet0/0/3 | DESI | FORWARDING | NONE
0 | GigabitEthernet0/0/4 | DESI | FORWARDING | NONE
12 | GigabitEthernet0/0/2 | DESI | FORWARDING | NONE
12 | GigabitEthernet0/0/3 | DESI | FORWARDING | NONE
12 | GigabitEthernet0/0/4 | DESI | FORWARDING | NONE
34 | GigabitEthernet0/0/2 | DESI | FORWARDING | NONE
34 | GigabitEthernet0/0/3 | DESI | FORWARDING | NONE
34 | GigabitEthernet0/0/4 | DESI | FORWARDING | NONE
Notes: A Layer 2 loop causes the following failures:
  An attempt to remotely log in to a device fails.
  An interface receives a large number of broadcast packets, which can be viewed in the display interface command output.
  An attempt to log in to a device through the serial port is time consuming.
  CPU usage exceeds 70%.
  High packet loss occurs when a ping command is used.
  The indicator of the VLAN interface with the loop occurring frequently blinks.
  A PC receives a large number of broadcast packets.
  A loop alarm is generated if loop detection is configured on a switch.

## Slide 41: PC1 and PC13 Cannot Communicate (6)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Check whether packet loss is caused by the loop. Check whether MAC address flapping detection is enabled on each involved switch and whether MAC address flapping is detected.
PC1
PC13
After observing for a while, find that the fault occurs during working hours. When the fault occurs, check the MAC address table, and find that the MAC address table is unstable. Then check STP statistics.
During working hours, a switch port frequently alternates between up and down, and sends a large number of TC BPDUs. In this case, configure the switch port connected to the PC as an edge port.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
[SW3]display mac-address flapping
Mac-address Flapping Configurations :
-------------------------------------------------
Flapping detection : Enable
Aging time(sec) : 300
Quit-vlan Recover time(min) : 10
Exclude vlan-list : -
-------------------------------------------------
<SW3>display mac-address flapping record
Info: The mac-address flapping record does not exist.
<SW3>display stp tc-bpdu statistics -------------------------- STP TC/TCN information --------------- |  |  | 
MSTID | Port | TC(Send/Receive) | TCN(Send/Receive)
12 | GigabitEthernet0/0/1 | 13/56 | -/-
12 | GigabitEthernet0/0/3 | 22/18 | -/-
12 | GigabitEthernet0/0/4 | 29/66 | -/-
Notes: After receiving STP TC BPDUs, the STP-enabled switch clears the MAC address table and re-learns MAC addresses. During this period, data forwarding is interrupted for a short period, causing packet loss.

## Slide 42: PC1 and PC13 Cannot Communicate (7)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
Shut down SW3's GE 0/0/4. PC1 cannot ping PC13, causing a large number of packets to be discarded in a short period. After SW3 is restarted, the following alarm is generated on SW3:
PC1
PC13
Port that obtains packet information
The IP address is a virtual IP address. VRRP may be defective. Obtain packet information on SW1's GE 0/0/10 and SW2's GE 0/0/3. The addresses marked bold are source MAC and IP addresses. SW2 fails to obtain data packet information.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
<SW3>
ARP/4/ARP_DUPLICATE_IPADDR(l)[0]:Received an
ARP packet with a duplicate IP address from the interface. (IpAddress=192.168.12.254, InterfaceName=Vlanif12, MacAddress=0000-5e00-0101)
[SW1]capture-packet interface GigabitEthernet 0/0/10 destination terminal
Packet: 6
-------------------------------------------------------
00 00 5e 00 01 03 54 89 98 1f 5a 8d 81 00 00 0c
08 00 45 00 00 3c 39 aa 40 00 80 01 11 b8 c0 a8
0c 01 c0 a8 22 0d 08 00 f9 d1 82 3b 0a 71 08 09
0a 0b 0c 0d 0e 0f 10 11 12 13 14 15 16 17 18 19
1a 1b 1c 1d 1e 1f 20 21 22 23 24 25 26 27
-------------------------------------------------------
Notes: The capture-packet command obtains information in service packets that match a configured rule. The obtained information is saved in a local file.
  capture-packet { interface interface-type interface-number | acl acl-number } * [ vlan vlan-id | cvlan cvlan-id ] * destination terminal [ car cir car-value | time-out time-out-value | packet-num number | packet-len length ] *
  Information in packets on the management interface cannot be obtained.
  This command can only obtain information received by an interface, not information sent by an interface.

## Slide 43: PC1 and PC13 Cannot Communicate (8)
SW1
SW2
SW3
SW4
GE0/0/10
GE0/0/3
GE0/0/4
GE0/0/3
GE0/0/4
GE0/0/10
As shown in the preceding slide, packets are dropped between SW1 and SW2, and the destination MAC address is 00 00 5e 00 01 03. The VRRP ID is 3, which should have been 1 as planned. Check the VRRP status and configuration of SW3.
PC1
PC13
According to the preceding analysis, a VRRP dual-master fault occurs because the VRID is incorrectly set. As a result, packet loss occurs during a VRRP switchover. Correct the configuration of SW3.
Carry out a reliability test again. Find that no packet loss occurs during the switchover. Then, the fault is rectified.
Physical link fault
Incorrectly configured IP address
VLAN configuration error
Loop
VRRP fault
<SW3>display vrrp
  Vlanif12 | Virtual Router 3
  State : Master
  Virtual IP : 192.168.12.254
  Master IP : 192.168.12.3
  PriorityRun : 100
  PriorityConfig : 100
  MasterPriority : 100
  Virtual MAC : 0000-5e00-0103
<SW3>display current-configuration interface Vlanif 12
  #
  interface Vlanif12
  ip address 192.168.12.3 255.255.255.0
  vrrp vrid 3 virtual-ip 192.168.12.254
Notes: The VRRP group numbers on SW3 and SW4 are different. After the VRRP group on SW3 detects a downlink fault, the VRRP status on SW4 does not change. The VRRP status on SW4 remains in the Master state. In this situation, sending gratuitous ARP messages is not triggered for an ARP entry update on the terminal.
The destination MAC address of data frames sent from PC1 to a gateway is still 00 00 5e 00 01 03.
After the link between SW1 and SW3 is disconnected, SW1 cannot forward packets to SW2, because SW1 does not have the MAC address entry of 00 00 5e 00 01 03.

## Slide 44
Troubleshooting Data Communication Network Faults
Troubleshooting Common Network Faults
  LAN Faults
  Route Faults
  Service Faults

## Slide 45: PC1 Cannot Use the FTP Service (1)
Simplified topology:
In the preceding example, measures are taken to ensure no fault occurs between PC1 and SW3 and between server 6 and SW5.
As shown in the figure on the left, possible causes for an FTP failure on PC1 are as follows:
  Physical link fault (done)
  Route faults
    Static route
    OSPF
    BGP
    IS-IS
  Traffic control fault
  Server fault (done)
This section describes how to troubleshoot route.
Planned traffic path
Server6
R1
R2
R3
SW1
SW3
SW6
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
IBGP
IBGP
PC1
Static
Static

## Slide 46: PC1 Cannot Use the FTP Service (2)
Static route
OSPF
IS-IS
BGP
Data packets are forwarded hop by hop. All routing devices along a path must have routes to the destination. First, check whether routes destined for server 6 exist on all devices through which data packets sent from PC1 to server 6 pass.
<SW3>display ip routing-table protocol static Route Flags: R - relay, D - download to fib ------------------------------------------------------------------------------ |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
0.0.0.0/0 | Static | 60 | 0 | RD | 10.0.13.1 | Vlanif13
Planned traffic path
Check the static route configuration on SW3.
    When configuring a static route, specify only the outbound interface name for a P2P interface. For a broadcast interface, also specify a next-hop IP address.
The command output indicates that the static route has been correctly configured on SW3.
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
Static

## Slide 47: PC1 Cannot Use the FTP Service (3)
Static route
OSPF
IS-IS
BGP
Check the routing table on R1.
Planned traffic path
The command output shows that R1 does not have a route to 192.168.56.0. Check whether a BGP peer relationship is properly established between R1 and R2.
The preceding command output shows that the BGP peer relationship fails to be established. Possible causes are as follows:
  The loopback0 interface of the remote device is unreachable.
  The AS number of the local or remote device is incorrect.
  The peer ebgp-max-hop command used to allow the establishment of an indirect EBGP peer relationship is not run.
  Router IDs on both ends are the same.
According to the command output, the numbers of sent and received BGP packets are 0, indicating that the loopback0 interface on the remote device may be unreachable.
<R1>display ip routing-table 192.168.56.0
<R1>display bgp peer BGP local router ID : 10.0.1.1 Local AS number : 100 Total number of peers : 1 Peers in established state : 0 |  |  |  |  |  |  | 
Peer | AS | MsgRcvd | MsgSent | OutQ | Up/Down | State | PrefRcv
10.0.2.2 | 100 | 0 | 0 | 0 | 0:00:05 | Idle | 0
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
Static

## Slide 48: PC1 Cannot Use the FTP Service (4)
Static route
OSPF
IS-IS
BGP
On R1, check the route destined for the BGP peer.
Planned traffic path
The command output shows that R1 does not have a route to 10.0.2.2. Check whether an OSPF neighbor relationship is properly established between R1 and R2.
The preceding command output shows that the OSPF neighbor relationship fails to be established. Possible causes are as follows:
  Router IDs on both ends are the same.
  Area IDs do not match on both ends.
  Network masks do not match on both ends.
  MTUs do not match on both ends.
  On an MA network, DR priorities of all devices are set to 0.
  Authentication passwords do not match on both ends.
  An interface is configured as a silent interface.
  Time parameters do not match on both ends.
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
Static
<R1>display ospf peer
OSPF Process 1 with Router ID 10.0.1.1
<R1>display ip routing-table 10.0.2.2

## Slide 49: PC1 Cannot Use the FTP Service (5)
Check OSPF error information on R1.
Static route
OSPF
IS-IS
BGP
Planned traffic path
The preceding command output shows that a router ID conflict may cause a failure to establish an OSPF neighbor relationship. To accurately locate the fault, enable OSPF debugging on R1.
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
Static
[R1]display ospf error
General packet errors:
0 : IP: received my own packet 0 : Bad packet
0 : Bad version 0 : Bad checksum
0 : Bad area id 0 : Drop on unnumbered interface
0 : Bad virtual link 0 : Bad authentication type
0 : Bad authentication key 0 : Packet too small
0 : Packet size > ip length 0 : Transmit error
0 : Interface down 0 : Unknown neighbor
0 : Bad net segment 0 : Extern option mismatch
133 : Router id confusion
<R1>terminal debugging
Info: Current terminal debugging is on.
<R1>debugging ospf packet interface GigabitEthernet 0/0/0

## Slide 50: PC1 Cannot Use the FTP Service (6)
Check the configuration of the local OSPF protocol.
Static route
OSPF
IS-IS
BGP
Planned traffic path
Check OSPF error information in the debugging information on R1. Some information is as follows:
After comparison, it is found that the interval at which Hello packets are sent, mask, and authentication information on one end matches those on the other end, and only the router ID conflict occurs.
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
<R1>display ospf interface GigabitEthernet 0/0/0 verbose
OSPF Process 1 with Router ID 10.0.1.1
Interface: 10.0.12.1 (GigabitEthernet0/0/0)
Cost: 1 State: DR Type: Broadcast MTU: 1500
Designated Router: 10.0.12.1
Backup Designated Router: 0.0.0.0
Timers: Hello 10 , Dead 40 , Poll 120 , Retransmit 5 , Transmit Delay 1
IO Statistics
Type Input Output
Hello 36 36
: Source Address: 10.0.12.2
: Destination Address: 224.0.0.5
: Ver# 2, Type: 1 (Hello)
: Length: 44, Router: 10.0.1.1
: Area: 0.0.0.0, Chksum: db9c
: AuType: 00
: Key(ascii): * * * * * * * *
: Net Mask: 255.255.255.0
: Hello Int: 10, Option: _E_
: Rtr Priority: 1, Dead Int: 40
Notes: The debugging information on R1 shows that the OSPF router ID carried in the Hello packets sent from 10.0.12.2 is the same as the OSPF router ID on R1.

## Slide 51: PC1 Cannot Use the FTP Service (7)
Log in to R2 and change the OSPF router ID. However, the attempt to use Telnet to log in to R2 fails.
Common causes of Telnet login failures are as follows:
  A route is unavailable, and a TCP connection cannot be established between the client and server.
  Telnet is disabled on the server.
  The number of users logging in to a device reaches a specified upper limit.
  An ACL is bound to a VTY user interface.
  An access protocol configured in the VTY user interface view is incorrect. If the protocol inbound ssh command is used, the attempt to use Telnet for login fails.
Log in to R2 through the console port and check whether Telnet is enabled.
Static route
OSPF
IS-IS
BGP
R1
R2
GE0/0/0
OSPF
Telnet
Check whether Telnet is allowed in the VTY view.
Modify the configuration of R2 to support Telnet in the VTY user interface view. The test result shows that the attempt to log in to R2 is successful.
[R2]display telnet server status
TELNET IPV4 server :Enable
TELNET IPV6 server :Enable
TELNET server port :23
[R2-ui-vty0-4]display this
user-interface vty 0 4
authentication-mode aaa
protocol inbound ssh

## Slide 52: PC1 Cannot Use the FTP Service (8)
Change the OSPF router ID on R2, restart the OSPF process to make the router ID take effect, and check the OSPF neighbor relationship status.
Static route
OSPF
IS-IS
BGP
Planned traffic path
Check whether the route to 10.0.2.2 exists on R1.
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Static
Static
<R2>display ospf peer
OSPF Process 1 with Router ID 10.0.12.2
Neighbors
Area 0.0.0.0 interface 10.0.12.2(GigabitEthernet0/0/0)'s neighbors
Router ID: 10.0.1.1 Address: 10.0.12.1
State: Full Mode:Nbr is Slave Priority: 1
DR: 10.0.12.2 BDR: 10.0.12.1 MTU: 0
Dead timer due in 35 sec
Retrans timer interval: 5
Neighbor is up for 00:09:17
Authentication Sequence: [ 0 ]
<R1>display ip routing-table 10.0.2.2 Route Flags: R - relay, D - download to fib ------------------------------------------------------------ |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
10.0.2.2/32 | OSPF | 10 | 1 | D | 10.0.12.2 | GE0/0/0

## Slide 53: PC1 Cannot Use the FTP Service (9)
Check the BGP peer relationship status on R1.
Static route
OSPF
Deploy IS-IS.
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Planned traffic path
Check whether the BGP routing table of R1 contains a route destined for 192.168.56.0/24.
R1 still does not have an available route. As R1 should have get the route from R3, check whether the route is imported into the BGP routing table on R3.
<R1>display bgp peer BGP local router ID : 10.0.1.1 Local AS number : 100 Total number of peers : 1 Peers in established state : 1 |  |  |  |  | 
Peer | AS | MsgRcvd | MsgSent | Up/Down | State
10.0.2.2 | 100 | 25 | 26 | 0:19:22 | Established
<R3>display bgp routing-table BGP Local router ID is 10.0.3.3 Total Number of Routes: 1 |  |  |  | 
Network | NextHop | MED | LocPrf | Path/Ogn
*> 192.168.56.0 | 0.0.0.0 | 0 | 0 | ?
<R1>display bgp routing-table BGP Local router ID is 10.0.1.1 Total Number of Routes: 2 |  |  |  | 
Network | NextHop | MED | LocPrf | Path/Ogn
*>192.168.12.0/24 | 0.0.0.0 | 0 | 0 | ?
Notes: On R3, the command output shows that the route to 192.168.56.0/24 has been imported into the BGP routing table.

## Slide 54: PC1 Cannot Use the FTP Service (10)
Check the BGP peer status on R3.
Static route
OSPF
IS-IS
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Planned traffic path
The BGP peer relationship is not established between R3 and R2. Check whether a route destined for 10.0.2.2/32 exists on R3.
R3 does not have the route to 10.0.2.2/32. As IS-IS runs between R2 and R3, check whether an IS-IS neighbor relationship is properly established between R3 and R2.
<R3>display ip routing-table 10.0.2.2
<R3>display bgp peer BGP local router ID : 10.0.3.3 Local AS number : 100 Total number of peers : 1 Peers in established state : 0 |  |  |  |  |  |  | 
Peer | AS | MsgRcvd | MsgSent | OutQ | Up/Down | State | PrefRcv
10.0.2.2 | 100 | 0 | 0 | 0 | 0:00:05 | Idle | 0
<R3>display isis peer Peer information for ISIS(1) |  |  |  |  | 
SystemId | Interface | CircuitId | State | Type | PRI
0100.0000.2002 | GE0/0/1 | 0100.0000.2002.01 | Up | L2 | 64
Notes: Possible causes for the failure to establish an IS-IS neighbor relationship are as follows:
  Area IDs do not match on both ends. (The inconsistency adversely affects only level-1 neighbor relationships.)
  IS-IS levels do not match on both ends. (Note that on Huawei devices if the system level differs from the interface circuit level, the system level takes effect.)
  Interface authentication settings do not match on both ends.
  System ID lengths do not match or system ID conflict occurs.
  The IP addresses are on different network segments. (Source check is enabled for IS-IS on a broadcast network, and can be disabled.)

## Slide 55: PC1 Cannot Use the FTP Service (11)
The IS-IS neighbor relationship is properly established, but R3 cannot obtain the route to 10.0.2.2/32. Possible causes are as follows:
  IS-IS is not enabled on an interface.
  Cost styles do not match on both ends.
  A routing policy is configured on the device.
  Network types do not match on both ends.
Check information about an IS-IS interface on R2.
Static route
OSPF
IS-IS
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
Check the IS-IS configuration on R2.
Planned traffic path
isis 1
is-level level-2
cost-style wide
network-entity 49.0001.0100.0000.2002.00
import-route ospf 1
<R2>display isis interface Interface information for ISIS(1) |  |  |  |  | 
Interface | Id | IPV4.State | MTU | Type | DIS
GE0/0/1 | 1 | Up | 1497 | L1/L2 | No/Yes
Loop0 | 1 | Up | 1500 | L1/L2 | --

## Slide 56: PC1 Cannot Use the FTP Service (12)
Check the IS-IS configuration on R3.
Static route
OSPF
Deploy IS-IS.
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
The following information shows that the cost style of R2 does not match that of R3. Change the cost style of R3 to wide. Then, check whether R3 has a route to 10.0.2.2/32.
Check whether the BGP peer relationship on R3 is restored and check the BGP routing table of R3.
Planned traffic path
isis 1
is-level level-2
network-entity 49.0001.0100.0000.3003.00
#
<R3>display ip routing-table 10.0.2.2 Route Flags: R - relay, D - download to fib -------------------------------------------------------------- |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
10.0.2.2/32 | ISIS-L2 | 15 | 10 | D | 10.0.23.2 | GE0/0/1
<R3>display bgp routing-table Total Number of Routes: 2 |  |  |  | 
Network | NextHop | MED | LocPrf | Path/Ogn
*>I 192.168.12.0 | 10.0.1.1 | 0 | 100 | ?
*> 192.168.56.0 | 0.0.0.0 | 0 | 0 | ?
<R3>display bgp peer BGP local router ID : 10.0.23.3 |  |  |  |  | 
Peer | AS | MsgRcvd | MsgSent | Up/Down | State
10.0.2.2 | 100 | 8 | 7 | 0:04:42 | Established

## Slide 57: PC1 Cannot Use the FTP Service (13)
R3 has correctly advertised routes and learned the route to 192.168.12.0/24. Check whether R1 has a route to 192.168.56.0/24.
Static route
OSPF
Deploy IS-IS.
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
R1 has received the BGP route from R3, but the route is unavailable. The possible cause is that the next hop is unreachable. On R1, check whether there is a route to 10.0.3.3/32.
The command output shows that the routing table of R1 does not contain the route to 10.0.3.3/32. This route should have been imported by R2 from IS-IS into the OSPF routing table. Possible causes are as follows:
  A routing policy is configured on R1.
  R2 does not import IS-IS routes into the OSPF routing table.
  Type 5 LSAs are filtered out in the outbound direction of R2's interface.
Planned traffic path
<R1>display ip routing-table 10.0.3.3
<R1>display bgp routing-table BGP Local router ID is 10.0.1.1 |  |  |  | 
Network | NextHop | MED | LocPrf | Path/Ogn
*> 192.168.12.0 | 0.0.0.0 | 0 | 0 | ?
I 192.168.56.0 | 10.0.3.3 | 0 | 100 | ?

## Slide 58: PC1 Cannot Use the FTP Service (14)
Check the LSDB of R1.
Static route
OSPF
Deploy IS-IS.
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
R1 does not have Type 5 LSAs. Check whether R1 imports IS-IS routes into the OSPF routing table.
Modify the configuration of R2, import IS-IS routes into the OSPF routing table, and then check the routing table of R1.
Planned traffic path
<R2>display current-configuration configuration ospf
#
ospf 1 router-id 10.0.2.2
area 0.0.0.0
network 10.0.2.2 0.0.0.0
network 10.0.12.2 0.0.0.0
#
<R1>display ospf lsdb OSPF Process 1 with Router ID 10.0.1.1 Area: 0.0.0.0 |  |  |  |  |  | 
Type | LinkStateID | AdvRouter | Age | Len | Sequence | Metric
Router | 10.0.2.2 | 10.0.2.2 | 5 | 48 | 80000003 | 1
Router | 10.0.1.1 | 10.0.1.1 | 3 | 48 | 8000000D | 1
Network | 10.0.12.1 | 10.0.1.1 | 3 | 32 | 80000002 | 0
<R1>display ip routing-table Route Flags: R - relay, D - download to fib ------------------------------------------------------------ |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
10.0.3.3/32 | O_ASE | 150 | 1 | D | 10.0.12.2 | GE0/0/0
192.168.56.0/24 | IBGP | 255 | 0 | RD | 10.0.3.3 | GE0/0/0
Notes: After the configuration of R2 is modified, the route to 10.0.3.3/32 is displayed on R1.

## Slide 59: PC1 Cannot Use the FTP Service (15)
Run the traceroute 192.168.56.6 command on PC1.
Static route
OSPF
Deploy IS-IS.
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
R3 does not respond to the received data packets. Enable traffic statistics collection on R3's GE 0/0/2 and check whether R3 sends the data packets through GE0/0/2.
GE0/0/2
Planned traffic path
traceroute to 192.168.56.6, 8
1 192.168.12.3 63 ms 46 ms 47 ms
2 10.0.13.1 78 ms 63 ms 62 ms
3 10.0.12.2 94 ms 63 ms 78 ms
4 10.0.23.3 94 ms 62 ms 63 ms
5 * * *
[R3] acl 3000
[R3-acl-adv-3000]rule 5 permit ip source 192.168.12.1 0 destination 192.168.56.6 0
[R3-acl-adv-3000]quit
[R3]traffic classifier trafficSta
[R3-classifier-trafficSta]if-match acl 3000
[R3-classifier-trafficSta]quit
[R3]traffic behavior trafficSta
[R3-behavior-trafficSta]statistic enable
[R3-behavior-trafficSta]quit
[R3]traffic policy trafficSta
[R3-trafficpolicy-trafficSta]classifier trafficSta behavior trafficSta
[R3-trafficpolicy-trafficSta]quit
[R3]interface GigabitEthernet0/0/2.35
[R3-GigabitEthernet0/0/2.35]traffic-policy trafficSta outbound
Notes: After R1 learns the route, PC1 still cannot access the FTP service provided by server 6. In this case, run the traceroute command to check connectivity between R1 and server 6.
Based on traffic statistics, the analysis is as follows:
  Check whether the traffic reaches the inbound interface of the device and determine whether packet loss occurs on the upstream device.
  Check whether the traffic is forwarded to the outbound of the device and determine whether packet loss occurs on the device.
  Check whether Layer 2 and Layer 3 information about traffic on the inbound interface of the device is correct and determine whether the upstream device forwards and encapsulates packets properly.
  Check whether the Layer 2 and Layer 3 information about the outbound interface is correct and determine whether the device forwards and encapsulates packets properly.
  Check whether transient traffic flapping occurs due to MAC address flapping, route changes, or IP address conflicts.
Procedure for configuring traffic statistics collection:
  Configure an ACL rule to match traffic to be collected.
  Configure a traffic classifier.
  Configure a traffic behavior and configure traffic statistics collection in the traffic behavior.
  Configure a traffic policy; bind the traffic classifier and behavior to the traffic policy; apply the traffic policy to the inbound direction of the switch to collect statistics on packets of different users.

## Slide 60: PC1 Cannot Use the FTP Service (16)
Check traffic statistics on R3. No packet loss occurs on R3.
Static route
OSPF
IS-IS
BGP
R1
R2
R3
SW3
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
GE0/0/2
Check the routing table of SW5 in the direction where server 6 sends data packets.
SW5 does not have a static route to PC1. Configure a static route on SW5.
Check whether PC1 and server 6 can communicate and use the FTP service properly.
After the preceding operations are complete, the troubleshooting is complete.
Planned traffic path
<R3> display traffic policy statistics interface GigabitEthernet0/0/2.35 outbound
Interface:GigabitEthernet0/0/2.35
Traffic policy inbound: trafficSta
Rule number: 1
Current status: OK!
Item Sum(Packets/Bytes)
-----------------------------------------
Matched 50/400
Passed 50/400
Dropped 0/0
[SW5]display ip routing-table |  |  |  |  |  | 
Destination/Mask | Proto | Pre | Cost | Flags | NextHop | Interface
10.0.35.0/24 | Direct | 0 | 0 | D | 10.0.35.5 | Vlanif35
192.168.56.0/24 | Direct | 0 | 0 | D | 192.168.56.5 | Vlanif56

## Slide 61: PC1 Cannot Use the FTP Service Summary
The following faulty points are involved in the troubleshooting:
  Incorrect static route configuration
  Failure to establish an OSPF neighbor relationship
  Incorrect IS-IS route calculation
  Failure to establish a BGP peer relationship
  Incorrect BGP route selection
  Telnet login failure
The following tools are used:
  packet information obtaining tool
  Traffic statistics collection tool
  Tracert
Planned traffic path
Server6
R1
R2
R3
SW1
SW3
SW6
GE0/0/1
GE0/0/0
OSPF
IS-IS
SW5
IBGP
IBGP
PC1
Static
Static

## Slide 62
Troubleshooting Data Communication Network Faults
Troubleshooting Common Network Faults
  LAN Faults
  Route Faults
  Service Faults

## Slide 63: PC5 Cannot Communicate with Any Host (1)
PC5 obtains an IP address using DHCP. The common causes of DHCP faults are as follows:
  The link between the client and server becomes faulty.
  The DHCP function is disabled on a device.
  The DHCP address allocation mode is not selected on a VLANIF interface.
  No IP address is available in an address pool.
Simplified topology:
DHCP relay agent
DHCP server
PC5
R3
SW6
SW5
GE0/0/4
GE0/0/2
GE0/0/10
PC5 cannot communicate with any host. The possible cause is that the physical link to PC5 is abnormal, or PC5's IP address is incorrect.
Check the IP address of PC5. PC5 fails to obtain an IP address.
PC>ipconfig | 
IPv4 address | 0.0.0.0
Subnet mask | 0.0.0.0
Gateway | 0.0.0.0
Physical address | 54-89-98-39-22-B7
DNS server | 0.0.0.0
Notes: If the client and server are on different network segments and a relay agent is deployed between them
  The link between the DHCP relay agent and server becomes faulty.
  The DHCP function is not enabled globally on a device. As a result, the DHCP function does not take effect.
  No DHCP server is specified on the DHCP relay agent.
  The DHCP relay agent and server are unreachable.

## Slide 64: PC5 Cannot Communicate with Any Host (2)
Check whether the physical link to PC5 is normal.
Check whether a Layer 2 loop occurs on SW6 and check the VLAN configuration.
PC5
R3
SW6
SW5
GE0/0/4
GE0/0/2
GE0/0/10
DHCP server
DHCP relay agent
VLAN
The preceding information shows that the physical status of GE 0/0/10 is normal, but GE 0/0/10 is configured as a trunk interface. Modify the configuration on SW6 to configure GE 0/0/10 as an access interface and set the VLAN ID to 56.
After the modification, check whether PC5 can properly obtain an IP address.
<SW6>display stp brief |  |  | 
MSTID | Port | Role | STPState
0 | GigabitEthernet0/0/4 | ROOT | FORWARDING
0 | GigabitEthernet0/0/10 | DESI | FORWARDING
0 | GigabitEthernet0/0/11 | DESI | FORWARDING
<SW6>display vlan
The total number of vlans is : 2
----------------------------------------------------------------
56 common TG:GE0/0/4(U) GE0/0/10(U) UT: GE0/0/11(U)
PC>ipconfig | 
IPv4 address | 0.0.0.0
Subnet mask | 0.0.0.0
Gateway | 0.0.0.0
Physical address | 54-89-98-39-22-B7
DNS server | 0.0.0.0

## Slide 65: PC5 Cannot Communicate with Any Host (3)
SW5 is a DHCP relay agent. Query the global configuration of SW5.
After the modification, PC5 still cannot obtain an IP address.
PC5
R3
SW6
SW5
GE0/0/4
GE0/0/2
GE0/0/10
DHCP server
DHCP relay agent
VLAN
The DHCP service has been enabled on SW5 and the DHCP relay agent has been configured. However, after the data packets sent by PC5 pass through SW6, SW6 adds the tag with VLAN ID 56 to the packets before forwarding them. As a result, the DHCP relay interface configured on SW5 is incorrect.
Modify the configuration of SW5:
<SW5>display current-configuration
dhcp enable
#
interface Vlanif35
ip address 10.0.35.5 255.255.255.0
dhcp select relay
dhcp relay server-ip 10.0.35.3
#
[SW5]interface Vlanif 56
[SW5-Vlanif56]dhcp select relay
[SW5-Vlanif56]dhcp relay server-ip 10.0.35.3

## Slide 66: PC5 Cannot Communicate with Any Host (4)
Query the DHCP relay status of SW5.
PC5
R3
SW6
SW5
GE0/0/4
GE0/0/2
GE0/0/10
DHCP server
DHCP relay agent
VLAN
SW5 has sent packets to the DHCP server, but does not receive any responses.
Check the DHCP server configuration on R3.
[SW5]display dhcp relay statistics
The statistics of DHCP RELAY:
DHCP packets received from clients : 11
DHCP DISCOVER packets received : 11
DHCP REQUEST packets received : 0
DHCP RELEASE packets received : 0
DHCP INFORM packets received : 0
DHCP DECLINE packets received : 0
DHCP packets sent to clients : 0
DHCP packets received from servers : 0
DHCP packets sent to servers : 11
<R3>display current-configuration
dhcp enable
#
ip pool test
gateway-list 192.168.56.254
network 192.168.56.0 mask 255.255.255.0
excluded-ip-address 192.168.56.6
dns-list 192.168.1.1
#
interface GigabitEthernet0/0/2
dhcp select global

## Slide 67: PC5 Cannot Communicate with Any Host (5)
R3 and SW5 are connected through sub-interfaces. Therefore, enable the DHCP server service on a sub-interface, instead of the physical interface GE0/0/2.
DHCP server
DHCP relay agent
VLAN
PC5
R3
SW6
SW5
GE0/0/4
GE0/0/2
GE0/0/10
PC5 has obtained an IP address and can use it to communicate with all hosts. The troubleshooting is complete.
Check the IP address on PC5.
After the preceding configurations are complete on R3, check the status of the DHCP server on R3.
[R3]interface GigabitEthernet 0/0/2.35
[R3-GigabitEthernet0/0/2.35]dhcp select global
<R3>display dhcp server statistics | 
DHCP Server Statistics: | 
Client Request | 2
Dhcp Discover | 1
Dhcp Request | 1
Server Reply | 2
Dhcp Offer | 1
Dhcp Ack | 1
Bad Messages | 0
PC>ipconfig | 
IPv4 address | 192.168.56.253
Subnet mask | 255.255.255.0
Gateway | 192.168.56.254
Physical address | 54-89-98-39-22-B7
DNS server | 192.168.1.1

## Slide 68
(Multiple-answer question) Which of the following causes are possible for a failure to establish an OSPF neighbor relationship? ( )
  Router ID conflict
  Area ID inconsistency
  Interface mask inconsistency
  Process ID inconsistency
(True or false) If the level of an interface on an IS-IS router is different from the global router level, the level of the interface takes effect. ( )
  True
  False
(Multiple-answer question) Which of the following faults may occur in case of a Layer 2 loop? ( )
  An attempt to remotely log in to a device fails.
  An interface receives a large number of broadcast packets, which can be viewed in the display interface command output.
  An attempt to log in to a device through the serial port is time consuming.
  CPU usage exceeds 70%.
Notes: ABC
B
ABCD

## Slide 69
The structured troubleshooting process involves fault report, fault confirmation, information collection, identification and analysis, cause listing, assessment, step-by-step troubleshooting, fault resolving, and wrap-up work.
The purpose of troubleshooting is to restore the proper service running status. First, determine a service traffic path before troubleshooting. The layered, comparison, block-based, segment-based, and replacement approaches are used.
On a LAN, the commonly used methods are to replace hardware to rectify link or device faults and to use STP to rectify LAN loops.
Network-layer faults are mainly caused by unavailable routes. This course describes the causes and troubleshooting procedures for the failures to establish OSPF and IS-IS neighbor relationships and BGP peer relationships.
Troubleshooting personnel must have abundant knowledge and be skilled in using multiple troubleshooting approaches. Troubleshooting experience summary also matters.