## Slide 1
Datacom
General
V1.0
Zhang Linrui/WX570554
2021.09.29
Shigeng Zhu/00261992 & Yueyue Lu/WX445705
New
2021.10.15
Update

## Slide 2: Enterprise Network Introduction

## Slide 3
Nowadays, data has become a new production factor and important asset of enterprises. Enterprise networks, as the infrastructure, promote the efficient transmission of various data and accelerate the digital transformation of thousands of industries.
Enterprise networks are classified into campus networks, wide area networks (WANs), and data center networks (DCNs). The three types of networks are used to meet different service requirements and have different network architectures.
This course introduces the general enterprise network architecture, enterprise networks in typical industries, and Huawei enterprise network solutions for specific scenarios.

## Slide 4
On completion of this course, you will be able to:
  Understand the overall architecture of enterprise networks.
  Understand the typical enterprise network architectures of different industries.
  Understand the relationship between Huawei datacom certification and enterprise networks.
  Understand Huawei enterprise network solutions.

## Slide 5
Enterprise Network Overview
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 6: “Power Grid” in the Digital World : Data Communication Network
The symbol of industrialization is "electricity", transmitting electricity through the power grid.
The symbol of digitalization is "cloudification", transmitting computing power through the cloud network.
Power generation system
Data communication network
Office
Production
Enterprise
Home
Terminal
Individual
e-Government cloud
Private cloud
Public cloud
Data center
Wind power
Hydropower
Coal power
Manufacturing
Transportation
Public services
Power grid
Power consumption end

## Slide 7: Enterprise Networks in the Digital Society
Office
Online meeting
Manufacturing
Campus network
After more than 30 years of development, networks have laid a solid foundation for the intelligent society. With the acceleration of enterprise digitalization, enterprise networks need to carry more and more key services, playing an important role in the digitalization process.
WAN
Internet
Private line
DCN
Other enterprise or personal networks
Computing
Storage
Security
O&M

## Slide 8: Enterprise Campus Network Overview
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
DC
A campus network is used to implement terminal access in a small range and interworking within an enterprise. Campus networks can be classified into small, midsize, and large ones based on the number of terminal users or NEs. A typical large campus network consists of the following modules:
Egress zone: the border between the campus internal network and external network. It is used for internal users to access the public network and for external users to remotely access the internal network.
Core layer: the core of campus data switching that connects all components of the campus network, such as the DC, management and O&M zone, and campus egress.
Aggregation layer: forwards horizontal traffic between users and vertical traffic to the core layer. The aggregation layer can function as the switching core of a department or area and can connect more terminals to the network.
Access layer: provides various access modes for users and is the first network layer to which terminals connect.
Terminal layer: involves various terminals that access the campus network, such as PCs, printers, IP phones, mobile phones, and cameras.
DC: deploys servers and application systems to provide data and application services for internal and external users of an enterprise.
Management and O&M zone: deploys the network management system (such as the NMS and authentication server) and O&M system.
Management and O&M zone

## Slide 9: Enterprise WAN Overview
District/County core
County-level MAN
WANs in the government, finance, electric power, railway, and civil aviation industries
Municipal core
Provincial core
WAN backbone network
An enterprise WAN connects the enterprise headquarters, branches, and data center for interconnection.
By users, enterprise WANs can be classified into self-built for internal use and self-built for external use.
  Self-built, for internal use: To meet the interconnection requirements of the headquarters, branches, and data centers in a large span, various industries such as large enterprise, government, finance, and electric power need to build their own WANs.
  Self-built, for external use: Carriers build WANs to provide WAN connection services for enterprises, including the Internet, MPLS private lines, and transmission private lines.
Generally, a WAN uses a hierarchical structure. For example, a WAN can be divided into the county-level MAN, municipal MAN, provincial core network, and backbone network. MANs at different levels provide access for networks in the current area and connect to the upper-level MAN or backbone network through the core network.

## Slide 10: Enterprise DCN Overview
Management and O&M zone
Test environment
zone 1
Test environment
zone 2
Production environment zone 1
Production environment zone 2
FW
FW
Leaf
FW
FW
WAN access zone
WAN
Switching core
Non-production extranet core
Internet
access zone
Campus access zone
Spine
VXLAN domain
VXLAN domain
VXLAN domain
VXLAN domain
Extranet
access zone
A DCN connects general-purpose computing, storage, and high-performance computing resources, carries communication between internal resources of the DC, and implements communication between the DC and external networks.
A mainstream DCN uses the spine-leaf architecture. Switches are connected through Layer 3 interfaces, and the underlay network runs a dynamic routing protocol. Traffic can be load balanced between spine and leaf nodes through equal-cost multi-path routing (ECMP), implementing a DCN that features high-bandwidth, non-blocking forwarding, and fast network convergence upon faults.
    To isolate services and tenants, VXLAN and EVPN technologies are deployed in DCs to build virtualized networks.
VTEP
Leaf
Leaf
Leaf
Spine
Spine
Spine
Border-Leaf
Border-Leaf
Border-Leaf
Border-Leaf
Production extranet core
Notes: DCNs do not have a fixed zone division mode. Different industries and enterprises have different area division modes.
The zone division in the slide uses the financial industry as an example:
  WAN access zone: connects to the WAN built by the enterprise.
  Campus access zone: accesses traffic from enterprise campus users.
  Extranet access zone: connects to external networks, such as networks of other enterprises and partners.
  Internet access zone: accesses user traffic from the Internet.
  Production environment zone: runs services.
  Test environment zone: provides services for external systems informally. Before a service is brought online to the production environment zone, the service is developed, tested, and verified in the test environment zone.

## Slide 11: Network Security Overview
Data center
Campus access
Administration
R&D
Marketing
IPS
Firewall
Sandbox
Anti-DDoS
Production environment 1
Production environment 2
Test environment 2
O&M management area
Internet
Guest
Firewall
Flow probe
WAF
SecoManager
Security controller
Log auditing
O&M auditing
Host antivirus software
NAC
DMZ
To improve efficiency and productivity, enterprises need more open ICT systems to support sharing and collaboration, which also causes security vulnerabilities and information leakage risks.
An enterprise network can use multiple methods to ensure its security. Common network security devices include anti-distributed denial of service (anti-DDoS) devices, HiSec Insight (security situational awareness system), and firewall, of which the firewall is the most common network security device. A firewall provides security features such as access control, identity authentication, data encryption, VPN technology, and NAT. Users can configure complex security policies based on their network environments to prevent unauthorized access and protect their networks.
Network egress
Notes: Different network security solutions can be used to cope with different network security problems.
  Deploying firewalls in the server area of a data center: implements security isolation, access control, and intrusion prevention between servers and VMs in the data center.
  Deploying Web Application Firewalls (WAFs) in the server area of a data center: protects website servers and prevents website text and images from being tampered with.
  Deploying anti-DDoS abnormal traffic detecting and cleaning devices: mitigates various DDoS attacks from the Internet.
  Deploying egress firewalls: performs security protection, such as NAT, application protocol identification and control, security isolation, and access control, to prevent unauthorized access.
  Implementing O&M auditing in the management area: centrally manages and controls accounts, authentication, authorization, and audit of various IT resources such as core service systems, hosts, databases, and network devices to comply with related laws and standards and implement unified access management and O&M audit of core resources.

## Slide 12
Notes:   Deploying Network Admission Control (NAC) for campus network access: performs authentication, authorization, and accounting (online behavior recording) on users who access the network, preventing unauthorized users from accessing core assets.
  Deploying HiSec Insight to work with multiple devices such as network devices, security devices, and flow probe devices: implements multi-dimensional closed-loop threat handling and prevents the threat scope from being expanded.
For more information about network security, see the Huawei Security certification series.

## Slide 13: Typical Enterprise Network: Education Industry
School campus DC
Internet
CERNET
Private line or VPN link
Main campus
Branch campus
Dormitory
Lecture hall
Library
Digital library
Distance education
Virtual experiment
Mobile learning
Take the campus network of a university in China as an example.
The campus network is a computer network that provides teaching, scientific research, and comprehensive information services for teachers and students (including their family members and visitors).
The higher education campus network refers to the campus network of higher education institutions.
The higher education campus network is generally divided into dormitories, living areas, teaching areas, and public areas. It provides wired and wireless network access services to help the campus enter the digital era and improve talent cultivation and innovation capabilities.
Internet
School campus network management
center
Multimedia classroom
Teaching building
Notes: China Education and Research Network (CERNET): a nationwide education and research computer network that is funded by the Chinese government and directly managed by the Chinese Ministry of Education. It is constructed and operated by Tsinghua University and the other leading Chinese universities.

## Slide 14: Typical Enterprise Network: Financial Industry
To meet their own business development and operation management requirements, financial enterprises generally build their own backbone networks across the country to support the development of enterprise informatization and core services.
The DC and its branches are connected through the backbone network. Network services are mainly centralized in the DC. Users are widely distributed inside and outside the banks. Branches access the DC of the head office through the backbone network.
P
P
P
DC A
DC B
DC N
Level-1 branch
Level-2 branch
Sub-branch
Financial backbone network

## Slide 15: Typical Enterprise Network: Transportation Industry
Core node
Aggregation node
Access node
Backbone network
Regional network
Ticket hall
OA
Video conferencing
PIS
GSM-R/wireless
CTC/RBC/TCC
The railway system in China is used as an example.
In the railway system, the network provides unified transmission services for signaling, dispatching, ticketing, integrated services, and GSM-R services.
The railway data communications network uses a two-layer architecture:
  A backbone network consisting of multiple high-performance core routers located at regional nodes and railway bureaus.
  A regional network set by each railway bureau. The regional network is connected to the backbone network through the backbone network's regional node of the local railway bureau to implement communication between railway bureaus.
As an independent autonomous system, the backbone network forwards traffic between the head office and railway bureaus and between railway bureaus.
Each railway bureau is configured with a backbone network access node and multiple backbone network forwarding nodes. The head office node functions as the service aggregation node of the entire railway system and does not forward traffic.
Head office node
Regional node 1
Regional node 2
Regional node N
Notes: Generally, the regional nodes of the backbone network are deployed in the equipment rooms of each railway bureau.
GSM-R: Global System for Mobile Communications - Railway
CTC: Centralized Traffic Control
RBC: Radio Block Center
PIS: Passenger Information System
TCC: Track Communications Center

## Slide 16: Typical Enterprise Network: Electric Power Industry
Provincial access network
P
P
P
Backbone layer
P
P
P
Provincial border
Backbone network
PE
PE
CE
Municipal access network
PE
CE
DR center
DR center
DR center
Provincial DC
Provincial companies, subordinate organizations, municipal companies, county access networks, MANS of municipal companies, and so on
Core layer
The electric power industry in China is as an example.
The electric power industry network is divided into two independent networks based on the carried services: dispatching network and integrated data network.
The dispatching network, as one of the core networks for electric power informatization, mainly carries power-related service control systems.
The integrated data network carries applications such as OA, production management, lightning weather information, and remote monitoring of unmanned substations. It is physically independent and parallel with the power dispatching network.
The integrated data network adopts a multi-level architecture, including the national backbone network, provincial integrated data network, and municipal integrated data network. The national backbone network is divided into the core layer (consisting of multiple core nodes deployed in the country) and the backbone layer (consisting of backbone nodes distributed in provincial companies in the country).
The data networks of provincial companies and branches are connected to the provincial border nodes of the backbone network to implement communication between provincial networks.

## Slide 17: Huawei Datacom Certification and Enterprise Network
HCIE-Datacom
Capability convergence
HCIP-Datacom-Campus Network Planning and Deployment
HCIP-Datacom-SD-WAN Planning and Deployment
HCIP-Datacom-WAN Planning and Deployment
HCIP-Datacom-Enterprise Network Solution Design
HCIP-Datacom-Advanced Routing Switching Technology
HCIP-Datacom-Network Automation Developer
HCIA-Datacom
HCIP-Datacom-Core Technology
Advanced datacom capabilities
Scenario-based network planning, construction, maintenance, and optimization capabilities
Basic datacom capabilities

## Slide 18
Enterprise Network Overview
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 19: Industry Digital Transformation, Improving Production Efficiency and Customer Satisfaction
Digital OA
Digital manufacturing
Source: According to Worldwide Digital Transformation 2019 Predictions released by IDC, "at least 55% of organizations will be digitally determined by 2020."
Source: IDC's 2018 manufacturing industry survey results shows that 84.9% manufacturing enterprises are undergoing digital transformation, driving business model innovations and reshaping the business ecosystem.
Digital education
Source: Gartner's 2019 CIO Agenda: Higher Education Industry Insights reveals that 86% of higher education CIOs would regard IT as a key factor in enabling education business transformation.
Always-online mass terminals/sensors, real-time production data collection, and automatic and precise control
All-wireless access, OA anytime and anywhere, one-click conference scheduling using an app, and automatic adjustment of lighting and temperature
Change from stuffing the duck to immersion, high-quality teaching resources on demand, and real-world teaching
DC
WAN
Campus Network

## Slide 20: In the Digital Era, How Campus Networks Support Digital Transformation Across Industries?
On-demand services
Quick service deployment and adjustment
Rapid rollout of value-added applications
Access anytime, anywhere
High-quality service transport
Ubiquitous connectivity
Accurate measurement and evaluation of user experience
AI-powered automatic adjustment of resource allocation
Perceptible experience
Service-based configuration delivery
Quick and accurate fault locating
Easy O&M
DC
WAN
Campus Network

## Slide 21: Service Requirements and Challenges of Large- and Medium-Sized Campus Networks
Converged transport
Requirements:
Access terminals and services are diversified, and a converged transport network is required.
Challenges:
Wi-Fi and IoT services are independently planned, deployed, and managed. The overall network construction cost is high.
The workload of network management and O&M is heavy.
User experience awareness
Requirements:
Network O&M needs to be automated and intelligent to perceive user experience anytime and anywhere.
Challenges:
Service faults cannot be detected in a timely manner.
After a fault occurs, the fault cause is determined based on the O&M experience of professional personnel, and the fault cannot be quickly located.
The network cannot be automatically optimized.
Network automation
Requirements:
Networks need to be automated to cope with the complexity of deployment and policies caused by the surge of applications and services.
Challenges:
The workload is repetitive and heavy, and manual configuration is complex.
New services need to be configured on devices one by one, which is time-consuming and costly.
The workload of network policy deployment and adjustment is heavy.
DC
WAN
Campus Network

## Slide 22: Service Requirements and Challenges of Small- and Medium-Sized Campus Networks
Plug-and-play network devices, improving deployment efficiency
The network configurations of multiple sites are centrally delivered, reducing onsite configuration and commissioning workload and improving deployment efficiency.
The network is plug-and-play and able to be expanded on demand, requiring low costs for upgrades.
Centralized O&M on the cloud, simplifying O&M of multiple sites
Scattered campus branch networks are centrally managed on the cloud through the Internet, and automation tools for troubleshooting, monitoring, and other management operations are integrated, implementing remote automated O&M.
Open APIs, accelerating integration of business applications
With open APIs and big data analytics capabilities, multiple management systems can be combined and interconnected to achieve unified network management. More value-added applications are available, leading enterprises into digital transformation.
Sites' network devices
Unified management and centralized configuration
Plug-and-play,
on-demand expansion
Centralized management of multiple branches on the cloud and remote automatic O&M
Site network 1
Site network 2
Site network N
Site network
Site network
Site network
Open and big data analytics capability
Cloud management platform
DC
WAN
Campus Network

## Slide 23: Development of Enterprise SD-WAN Technologies
Migration of enterprise services to the cloud
Enterprise services are migrated to the cloud, and enterprise egress traffic increases sharply.
Proportion of egress traffic to total traffic on the enterprise network
Source: IDC
Intelligence
Cloudification
Video
Mobility
2016
2020
20%
80%
Emergence of Software defined networking (SDN)
Unified management and centralized configuration
High-speed development of the Internet
Rapidly narrowing gap between the quality of the Internet and traditional private lines
The coverage and network performance of the Internet are continuously improving, and the gap between the quality of the Internet and traditional private lines is narrowing rapidly. As such, more and more enterprises and organizations are using the Internet for interconnection.
Traditional carrier private lines/MPLS
Internet
SDN introduces a new role, that is, the centralized controller, so that it can not only understand the network requirements proposed by the administrator, but also fully manage and configure the physical network, implementing automatic deployment and fast provisioning of applications on the network.
DC
WAN
Campus Network

## Slide 24: Service Requirements and Challenges of Multi-Campus Network Interconnection
Service provisioning period
Service experience
Management and O&M
Unified management
Branch interconnection cost
Requirements:
The cost of WAN interconnection between branches needs to be reduced.
Challenges:
Carriers' transmission private lines or MPLS VPN private lines are of high quality but expensive.
Requirements:
The network deployment efficiency needs to be improved and the service provisioning period needs to be shortened.
Challenges:
It takes a long time to provision traditional private lines.
Service provisioning is mainly performed by network engineers on site, which has high skill requirements and low efficiency.
Requirements:
The application identification capability needs to be enhanced to ensure key service experience.
Challenges:
Different enterprise applications have different requirements on link quality.
Traditional private lines cannot detect the application status and cannot guarantee key services at any time.
Requirements:
Visualized O&M is required to simplify management and O&M.
Challenges:
CLI-based O&M is inefficient and lacks visualized O&M methods.
If an enterprise has a large number of branches, onsite O&M will increase costs.
Requirements:
LAN-side and WAN-side services need to be managed in a unified manner.
Challenges:
Unified configuration management and O&M cannot be implemented.
DC
WAN
Campus Network

## Slide 25: Cloud + Intelligence, Accelerating HPC
Supercomputing — the core of high-performance computing (HPC) — provides the computing power needed to drive development of the digital economy and plays a key role in numerous scientific and technological fields.
Speed is still the primary factor in supercomputing realizing faster and more accurate computing and simulation. This is where cloud and intelligence come in. In addition, the supercomputing of cloudification and artificial intelligence is gradually integrated, which poses higher requirements on the DCN that carries supercomputing services.
Weather forecast
21.8% -> 90%
Weather forecast accuracy
Life science
13 years -> 1 day
Gene sequencing duration
Drug R&D
500 days -> 100 days
New drug R&D and identification
Supercomputing center
Cloud
High-performance computing
Intelligence
Network requirements
Cloud-network synergy
Fast deployment
High-speed interconnection
Zero delay
Low packet loss rate
DC
WAN
Campus Network

## Slide 26: Three IT transformations, Driving Full Ethernet Evolution of DCNs
With the development of enterprise digital transformation, data has become a key production factor. DCs are responsible for data computing, storage, and forwarding, and are the most critical digital infrastructure in the new infrastructure. The IT architecture, computing, and storage of DCs are undergoing significant changes, driving DCNs to evolve from the multi-protocol mode to the full-Ethernet mode.
100x
Scale
Centralized -> Distributed
IT architecture
Computing unit
Storage media
PCIE
IB
Ethernet
CPU/GPU Ethernet interconnection
100x
Performance
or
AS-IS
TO-BE
1000x
Capacity
SCSI
NVMe
FC (32G)
RoCE (400G)
PCIe is removed
HDD -> SSD
All-flash storage Ethernet interconnection
Server Ethernet interconnection
Ethernet
Ethernet
Centralized
Distributed
DC
WAN
Campus Network
Notes: InfiniBand (IB): an input/output (I/O) switching technology that uses a central InfiniBand switch to establish a single link between remote storage devices, networks, and servers as well as to direct traffic. It has a compact structure, greatly improving system performance, reliability, and effectiveness, and relieving data traffic congestion between hardware devices.
Remote Direct Memory Access over Converged Ethernet (RoCE): a network protocol that allows remote direct memory access (RDMA) over the Ethernet. There are two RoCE versions: RoCEv1 and RoCEv2. RoCEv1 is a data link layer protocol that allows any two hosts in the same Ethernet broadcast domain to communicate with each other. RoCEv2 is a network layer protocol and its packets can be routed.

## Slide 27: Three Challenges Facing DCN Full-Ethernet Evolution
More complex for large-scale network O&M
Zero packet loss required for dual-active storage
Zero packet loss required for high-performance computing
The packet loss rate increases exponentially with the increase of network nodes on traditional Ethernet.
Traditional Ethernet lacks effective O&M methods,
and the network is too complex to be handled manually.
0.2–0.3% packet loss rate
The delay increases in intra-city (long distance) transmission, and it is difficult to perform flow control across DCNs on traditional Ethernet.
0.15%
0.02%
>70 km
DC A
DC B
1000 nodes, million-level configuration
DC
WAN
Campus Network

## Slide 28: 5G + Cloud, Increasingly Complex WAN Transport Services
With the advent of the 5G and cloud era, various innovative services such as VR/AR, live streaming, and autonomous driving are emerging. The traffic on the entire network increases explosively, and the dynamic complexity of services also increases the complexity of the entire network.
Enterprise campus, DC, and branch
WAN
MANs at all levels
4K
DC
WAN
Campus Network

## Slide 29: Service Requirements and Challenges Facing the WAN
Slow service provisioning
High SLA requirements
Complex O&M
The network passively adapts to various new services, such as enterprise private line services. Service provisioning is time-consuming and customer response is slow.
With the development of new services such as enterprise application migration to the cloud, network traffic in carriers' pipes is more dynamic and unpredictable. Traditional network planning and optimization have poor adaptability, and service SLA assurance faces great challenges.
As the network scale and complexity increase, the O&M complexity also increases. Carriers urgently need to deploy automation measures to reduce the skill requirements for O&M personnel and effectively control the OPEX in the long term.
Network policy
Service requirements
< 1s
10s
Failover time
L3VPN
L2VPN
DC
WAN
Campus Network
Notes: Service Level Agreement (SLA): an agreement between a service provider and a user. The SLA defines the service type and quality provided by the service provider for the user, and the commitment to the performance and reliability of the user assurance service. For example, the SLA ensures that the service reliability is higher than 99.99%, the fault response time is within 30 minutes.
Operating Expense (OPEX): the sum of the maintenance cost, marketing expense, labor cost, and depreciation expense during the enterprise operations.

## Slide 30
Enterprise Network Overview
Trends and Challenges of Enterprise Networks
Huawei Enterprise Network Solutions

## Slide 31: Huawei Intelligent Cloud-Network Solution
Network security
HiSec
Hyper-converged DCN
CloudFabric 3.0
CloudWAN
CloudWAN 3.0
CloudCampus
CloudCampus 3.0
Campus
General computing
Storage
HPC
AR
Switch
AP
Intra-cloud interconnection
All-Ethernet-based high-performance computing (HPC) and storage
Inter-cloud interconnection
Flexible migration to the cloud
SLA experience assurance
Cloud access
All-wireless campus
High-quality experience
Cloud-network-security collaboration

## Slide 32: Four Engines + Platform for Manager, Controller, and Analyzer Convergence
AirEngine
CloudEngine
NetEngine
HiSecEngine
WLAN
Switch
Router
Network security
iMaster NCE
Management, control, and analysis convergence platform

## Slide 33: Huawei CloudCampus Solution: CloudCampus 3.0
Campus network
DC
WAN
Branch
HQ
Wired network as a supplement
Office
Monitoring
Production
All-wireless networking
The AirEngine 8760 supports 16T16R, with no coverage holes and no frame freezing.
The PCC optical/electrical hybrid cable provides ultra-high bandwidth.
Intelligent O&M
iMaster NCE-CampusInsight supports user experience visualization.
LAN/WAN wired intelligent O&M enables fault locating within minutes.
SD-WAN intelligent traffic steering technology, improving link utilization.
SRv6 technology, one-hop connection to the cloud.
One global network
  Network-wide automation | AI-powered intelligent O&M
...
SD-WAN
Public/Private cloud
Cloud management
iMaster NCE supports auto scaling and can manage up to 200,000 NEs concurrently.
A single controller supports end-to-end SDN automation for the WAN, LAN, and WLAN.
Notes: In the campus network scenario, iMaster NCE-Campus is used as the iMaster NCE controller.

## Slide 34: Huawei Hyper-Converged DCN Solution: CloudFabric 3.0
Full-lifecycle automation
TTM reduced by 90%
Network-wide intelligent O&M
Complaints reduced by 75%
Active-active all-Ethernet storage network
Cross-DC links reduced by 90%
Unleashes 100% of computing power
All-Ethernet HPC network
Multi-cloud
Automation
Intelligence
General Computing
Storage
HPC
Controller
Analyzer
Manager
Hyper-converged DCN
Campus network
DC
WAN
Notes: In the data center scenario, iMaster NCE-Fabric is used as the iMaster NCE controller.

## Slide 35: Huawei CloudWAN Solution: CloudWAN 3.0
Integrated cloud-network-security operations
Qiankun security cloud service
Cloud management platform
"Added" for "connectivity"
"Adjusted" for "quality"
"Born" for "cloud"
Intelligent MAN
Intelligent cloud backbone
Government
Education
Healthcare
Manufacturing
Network as a service
Flexible multi-cloud connection
Cloud-network-security collaboration
Deterministic experience
Network as a service
Network as a service, one-stop provisioning of cloud-network products
OSS and BSS streamlining, easy to integrate
Flexible multi-cloud connection
Pre-connection to multiple clouds
End-to-end SRv6, access to the cloud upon network access
Deterministic experience
Slices for deterministic SLAs
One network for multiple industries with secure isolation
Cloud-network-security collaboration
Four-dimensional integrated security protection
AI-powered threat correlation detection
Cloud-network management and control
Campus network
DC
WAN
Notes: In this scenario, iMaster NCE-IP is used as the iMaster NCE controller.

## Slide 36: What Is iMaster NCE?
iMaster NCE is a network automation platform that integrates management, control, analysis, and AI capabilities.
3
4
2
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting
Automated + Intelligent
Manage + Control + Analyze
Plan + Construct + Maintain + Optimize
Unified data base
Centralized detection and locating
Full lifecycle management
Simulation/Verification/Monitoring/Optimization
Network management system
Controller
Analyzer
=
Autonomous driving network system
Network

## Slide 37: All-New iMaster NCE
DC
iMaster NCE-Fabric
Enterprise campus
iMaster NCE-Campus
SD-WAN
iMaster NCE-WAN
WAN transmission
iMaster NCE-T
IP WAN
iMaster NCE-IP

## Slide 38
(Multiple-answer question) Which of the following controllers have the SD-WAN feature? ( )
  iMaster NCE-Campus
  iMaster NCE-WAN
  iMaster NCE-IP
  iMaster NCE-SD-WAN
Notes: AB

## Slide 39
This course briefly introduces the overall enterprise network architecture and the campus networks, DCNs, and WANs in different scenarios.
With the continuous development of services and new technologies, enterprise networks are facing great challenges. Therefore, Huawei provides corresponding solutions for networks in different scenarios. These contents will be described in more details in subsequent courses.