## Slide 1
Datacom
General
V1.0
Wan Changli/WX408647
2020.06.06
Zhu Shigeng/00261992
Update
Shi Miaomiao/WX791350
2021.01.15
Zhu Shigeng/00261992
Update
Lu Yueyue/WX445705
2021.10.15
He Junjian/WX580230
Update

## Slide 2: VXLAN and Campus Network Virtualization

## Slide 3
Virtual eXtensible Local Area Network (VXLAN), defined in RFC 7348, is a Network Virtualization over L3 (NVO3) technology that uses MAC-in-User Datagram Protocol (MAC-in-UDP) encapsulation.
VXLAN has been widely used on data center networks (DCNs). As campus networks have increasingly flexible service requirements and growing virtualization and network automation requirements, VXLAN is introduced to campus networks and works with the SDN controller to provide more benefits for customers.
This course describes basic concepts and fundamentals of VXLAN and how to use VXLAN to build a multi-purpose campus network.

## Slide 4
On completion of this course, you will be able to:
  Describe the network requirements of VM live migration in the data center (DC) scenario and how VXLAN meets these requirements.
  Describe basic concepts of VXLAN.
  Describe fundamentals of VXLAN.
  Describe the application of VXLAN in campus network virtualization scenarios.
  Describe the application of BGP EVPN in campus network virtualization scenarios and how BGP EVPN works with VXLAN.

## Slide 5
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
BGP EVPN
Campus Network Virtualization

## Slide 6: Technical Background: Virtualization Are Widely Deployed by Enterprises
Virtualization technologies reduce IT costs, improve service deployment flexibility, and reduce O&M costs. More and more enterprises choose to use cloud computing or virtualization technologies in their DCs or campus IT infrastructure.
After an enterprise chooses the virtualization architecture, services are deployed on VMs in server clusters.
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Web 1
DB
APP
Services are deployed on VMs in server clusters.
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Web 2
DB
APP
Cluster
Physical network

## Slide 7: New Network Requirement: Layer 2 Extension
VMs in a virtualization or cloud computing cluster can be migrated flexibly. As a result, VMs running the same service (on the same network segment) may run on different servers, or the same VM (with the same IP address) may run on different servers (physical locations) at different times.
Physical servers may be located in equipment rooms with long geographical distances. Therefore, Layer 3 interconnection is required.
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Web 1
DB
APP
Layer 2 communication over a Layer 3 network
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Web 2
DB
APP
Cluster
Layer 2 communication is required for the same service.
Physical network (Layer 3)
Notes: After servers are virtualized, services are encapsulated in VMs. VMs can be live migrated to any host in a cluster. One of the features of live migration is that the network status does not change. As a result, the IP addresses of service VMs may be in different network locations. Therefore, a large Layer 2 network is required to solve this problem.

## Slide 8: New Network Requirement: Multi-Tenant Isolation
In cloud-based scenarios, multi-tenancy is supported, that is, different tenants share physical resources. This poses two requirements on the network: inter-tenant isolation and intra-tenant communication.
  Inter-tenant isolation: Tenants may be configured with the same MAC address and IP address. Therefore, physical network isolation needs to be considered. In addition, a large number of potential tenants need to be isolated.
  Intra-tenant communication: VMs on the same network segment of a tenant require Layer 2 communication, which is irrelevant to physical locations.
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Tenant 1
Tenant 2
Tenant 3
Server
Hypervisor
Guest OS
Guest OS
Guest OS
Tenant 1
Tenant 2
Tenant 3
Physical network (Layer 3)
Intra-tenant Layer 2 communication
Cluster
Inter-tenant network isolation

## Slide 9: Challenges Facing Traditional Networks
VM quantity limited by entry specifications of devices
Server virtualization leads to an exponential growth of the number of VMs, compared with physical servers. However, the MAC address table size of a Layer 2 device at the access side is incapable to meet this change.
Limited network isolation capabilities
The VLAN ID field has only 12 bits.
The number of tenants is much greater than the number of available VLANs in large virtualization and cloud computing service scenarios.
VLANs on traditional Layer 2 networks cannot adapt to dynamic network adjustment.
Limited VM migration scope
VM migration must be performed on a Layer 2 network.
VM migration on a traditional Layer 2 network is limited to a small scope.
Large numbers of VMs
Each device must have a large MAC address table.
Destination
MAC
Source
MAC
802.1Q
Tag
Length/
Type
Payload
FCS
802.1Q-tagged frame
The 12-bit VLAN IDs can represent only 4096 logical units.
The number of tenants supported by a large DC is much greater than 4096.
DC
VMs can be migrated only within a VLAN. The number of VLANs is limited.
Migration
End-to-end
VLAN
Notes: VXLAN is used to meet requirements of DCNs. On traditional enterprise campus networks, VXLAN is used to construct virtual networks instead of solving some urgent problems.

## Slide 10
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
  Basic Concepts
  Fundamentals
  Basic Configuration
BGP EVPN
Campus Network Virtualization

## Slide 11: Overview of VXLAN
VXLAN is essentially a virtual private network (VPN) technology and can be used to build a Layer 2 virtual network over any networks with reachable routes. VXLAN uses VXLAN gateways to implement communication within a VXLAN network and communication between a VXLAN network and a non-VXLAN network.
VXLAN utilizes MAC-in-UDP encapsulation to extend Layer 2 networks. It encapsulates Ethernet packets into IP packets for these Ethernet packets to be transmitted over routes, without considering the MAC addresses of VMs. In addition, the routed network has no limitation on the network structure and supports large-scale expansion. As such, VM migration is not constrained by the network architecture.
Underlay
Local LAN
VXLAN tunnel
Overlay
Local LAN
Local LAN
Notes: VXLAN solves the following problems on traditional networks:
  For VM quantity limited by entry specifications of devices.
    VXLAN encapsulates original data packets sent from VMs in the same domain into UDP packets, with the IP and MAC addresses used on the physical network in outer headers. Devices on the VXLAN network are aware of only the encapsulated parameters but not the inner data.
    Except VXLAN edge devices, other devices on the network do not need to identify MAC addresses of VMs. This reduces the burden of learning MAC addresses and improves device performance.
  For limited network isolation capabilities.
    VXLAN uses a VXLAN Network Identifier (VNI) field similar to the VLAN ID field to identify users. The VNI field has 24 bits and can identify up to 16 million VXLAN segments, effectively isolating a large number of tenants.
  For limited VM migration scope.
    VMs using IP addresses in the same network segment are in a Layer 2 domain logically, even if they are on different physical Layer 2 networks. VXLAN technology constructs a virtual large Layer 2 network over a Layer 3 network.
Underlay network: a physical network, which serves as the basic layer of the upper-layer logical network.
Overlay network: a logical network established on the underlay network using tunneling technologies.

## Slide 12: Application of VXLAN in DCs
VXLAN can be applied to a DCN that uses a spine-leaf two-layer physical architecture.
Spine nodes forward traffic based on routes and are unaware of the VXLAN tunnel during traffic forwarding. Leaf nodes provide network access for device resources such as servers, and perform VXLAN encapsulation and decapsulation.
All services in the DC are carried by the VXLAN network.
Layer 3 interconnection links without Layer 2 loops
Dynamic routing protocols for network reachability
Physical network
Spine-leaf architecture and VXLAN
VXLAN
On-demand VXLAN tunnel establishment
Upper-layer service network
Spine
Spine
Leaf
Leaf
Leaf

## Slide 13: Using VXLAN to Build a Multi-Purpose Campus Network
Multiple services carried on one network
Internet
OA
Videoconferencing
Security
protection
Internet
OA
Videoconferencing
Security protection
VXLAN
VN1
OA VN
VN2
Videoconferencing VN
VN3
Security protection VN
OA
Videoconferencing
Security
protection
Notes: The virtualization technology is introduced to create multiple virtual networks (VNs) on a physical network on a campus network. Different VNs are used for different services, such as OA, videoconferencing, and security protection.

## Slide 14: Why VXLAN Is Used to Implement Campus Network Virtualization?
A VXLAN network can be built on any complex Layer 3 network.
Layer 3 virtual network supported
VXLAN works with the SDN controller to implement centralized deployment and automation. There are successful practices.
Technology | Underlay Network | Overlay Network | Configuration and Management | Carrying User Group Information | Networking Requirements
VLAN | Layer 2 | Layer 2 | CLI or controller-based | None | Widely supported by devices.
MPLS VPN | Layer 3 | Layer 2/Layer 3 | Carrier-level technology requirements | None | End-to-end MPLS must be supported.
VXLAN | Layer 2/Layer 3 Built on any physical network | Layer 2/Layer 3 | CLI or controller-based | Supported | Nodes at both ends of a tunnel support VXLAN.

## Slide 15: VXLAN Packet Format
Outer
Ethernet header
Outer
IP header
UDP header
VXLAN
header
Inner
Ethernet header
Inner
IP header
Payload
Original data frame
VXLAN encapsulation
VXLAN Flags
(00001000)
Reserved
VNI
Reserved
8 bits
24 bits
24 bits
8 bits
Source UDP port
(Hash value)
Destination UDP port (4789)
Length
Checksum
Source IP address: IP address of the source VTEP of a VXLAN tunnel
Destination IP address: IP address of the destination VTEP of a VXLAN tunnel
Notes: The preceding packet format is a standard VXLAN packet format. Huawei CloudEngine S series switches use customize reserved fields based on the standard one.

## Slide 16: Basic Concepts of VXLAN: NVE
Network Virtualization Edge (NVE):
  A network entity that implements network virtualization functions. A physical or software switch can work as an NVE.
  NVEs run VXLAN and construct a Layer 2 virtual network over a Layer 3 network. SW1 and SW2 in the figure are NVEs.
SW1 (NVE)
SW2 (NVE)
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
IP network
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge

## Slide 17: Basic Concepts of VXLAN: VTEP
VXLAN tunnel endpoint (VTEP):
  A VTEP is located on an NVE and encapsulates and decapsulates VXLAN packets.
  In the outer IP header of VXLAN packets, the source IP address is the IP address of the source VTEP, and the destination IP address is the IP address of the destination VTEP.
SW1
SW2
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
IP header
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
IP header
Payload
Ethernet header
Source IP address: 1.1.1.1
Destination IP address: 2.2.2.2
Original data frame
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge
Notes: A pair of VTEP IP addresses identifies a VXLAN tunnel.
The source VTEP encapsulates packets and sends the encapsulated packets to the destination VTEP through the VXLAN tunnel. After receiving the encapsulated packets, the destination VTEP decapsulates the packets.
Generally, the IP address of a loopback interface on a device is used as the VTEP address.

## Slide 18: Basic Concepts of VXLAN: VNI and BD
VXLAN Network Identifier (VNI):
  VNIs are similar to VLAN IDs and are used to differentiate VXLAN segments. VMs in different VXLAN segments cannot communicate with each other at Layer 2.
  A tenant can have one or more VNIs. The VNI field has 24 bits.
BD 20
VNI 2000
BD 20
VNI 2000
SW1
SW2
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
IP header
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
IP header
Payload
Ethernet header
VNI: 2000
Original data frame
Bridge domain (BD):
  VLANs are used to divide broadcast domains on a traditional network. Similarly, BDs are used to divide broadcast domains on a VXLAN network. A BD identifies a large Layer 2 broadcast domain on a VXLAN network.
  VNIs are mapped to BDs in 1:1 mode. Terminals in the same BD can communicate with each other at Layer 2.
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge

## Slide 19: Basic Concepts of VXLAN: VAP
Virtual access point (VAP):
  A VAP implements VXLAN service access. A VAP can be configured in Layer 2 sub-interface mode or VLAN binding mode:
    Layer 2 sub-interface: In this example, a Layer 2 sub-interface is created on SW1 and associated with BD 10, indicating that only specific traffic on the sub-interface is forwarded to BD 10.
    VLAN binding: In this example, VLAN 10 is configured on SW2 and associated with BD 10, indicating that all traffic from VLAN 10 is forwarded to BD 10.
SW1
SW2
PC1
192.168.1.1/24
Layer 3 link
Layer 3 link
PC2
192.168.1.2/24
VXLAN tunnel
G0/0/1.1
Bind it to BD 10
BD 10
Bind it to VLAN 10
1
2
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge
Notes: After traffic from a traditional network enters a VXLAN network, a Layer 2 sub-interfaces or VLAN is bound to a BD. A VXLAN VNI is specified in the BD to implement mapping from the traditional VLAN network to the VXLAN network.

## Slide 20: Basic Concepts of VXLAN: Border and Edge Nodes
Edge: an edge access device on a VXLAN network, through which traffic from a traditional network enters the VXLAN network.
Border: a node for communication between a VXLAN network and an external network. It is used for external traffic to enter the VXLAN network or internal traffic to access the external network. It is usually connected to devices (such as routers and firewalls) that have Layer 3 forwarding capabilities.
VXLAN network
External network
Edge
Edge
Border
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge

## Slide 21: Basic Concepts of VXLAN: Layer 2 and Layer 3 VXLAN Gateways
Edge1
Layer 2 gateway
Edge2
Layer 2 gateway
Border
PC1
192.168.1.1/24
PC2
192.168.1.2/24
Layer 2 gateway: forwards traffic to a VXLAN network or is used for intra-subnet communication on the same VXLAN network.
Edge1
Layer 2 gateway
Edge2
Layer 2 gateway
Border
Layer 3 gateway
PC1
192.168.1.1/24
PC2
192.168.2.2/24
Layer 3 gateway: is used for inter-subnet communication on a VXLAN network and allows access to an external network (non-VXLAN network).
VXLAN tunnel
VXLAN tunnel
VXLAN tunnel
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge

## Slide 22: Basic Concepts of VXLAN: VBDIF Interface
VBDIF 10
192.168.1.254
VBDIF 20
192.168.2.254
SW1
Layer 2 gateway
SW2
Layer 2 gateway
SW3
Layer 3 gateway
BD 10 (VNI 1000)
BD 20 (VNI 2000)
VLANIF interfaces are used for communication between broadcast domains on a traditional network. Similarly, VBDIF interfaces are used for communication between BDs on a VXLAN network.
A VBDIF interface is a Layer 3 logical interface created for a BD on a Layer 3 VXLAN gateway.
IP addresses can be configured for VBDIF interfaces to implement communication between different VXLAN segments and between VXLAN and non-VXLAN networks, and to connect a Layer 2 network to a Layer 3 network.
PC1
192.168.1.1/24
PC2
192.168.2.2/24
VXLAN tunnel
VXLAN tunnel
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge

## Slide 23: Basic Concepts of VXLAN: Distributed and Centralized Gateways
Layer 3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
Layer 2 gateway
PC2
192.168.2.1/24
Layer 2 gateway
The Layer 3 gateway is deployed on one device. All inter-subnet traffic is forwarded by the gateway to implement centralized traffic management.
VTEPs function as both Layer 2 and Layer 3 gateways. Non-gateway nodes are unaware of VXLAN tunnels and only forward VXLAN packets.
Centralized gateway
Distributed gateways
Layer 2/Layer 3 gateway
Layer 2/Layer 3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
PC2
192.168.2.1/24
NVE
VAP
Gateway
VNI and BD
VTEP
Border and Edge
Notes: Centralized gateway:
  Advantage: Inter-subnet traffic is managed in a centralized manner, simplifying gateway deployment and management.
  Disadvantage: The forwarding path is not optimal. The ARP entry specification is a bottleneck. Because a centralized Layer 3 gateway is deployed, ARP entries must be generated on the gateway for terminals whose traffic is forwarded through the gateway.
Distributed gateways:
  Advantage: VTEPs only need to learn ARP entries of terminals connected to them, which eliminates the ARP entry specification bottleneck in the centralized Layer 3 gateway scenario and improves the network scalability.
  Disadvantage: Gateway deployment in this scenario is more complex than that in the centralized gateway scenario.

## Slide 24
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
  Basic Concepts
  Fundamentals
  Basic Configuration
BGP EVPN
Campus Network Virtualization

## Slide 25: VXLAN Tunnel Establishment Modes
A VXLAN tunnel is identified by a pair of VTEP IP addresses. Packets are encapsulated on VTEPs and then transmitted based on routes in the VXLAN tunnel. After a VXLAN tunnel is configured, it can be established successfully as long as the VTEPs at both ends of the tunnel have reachable routes to each other's IP address at Layer 3.
VXLAN tunnels are classified into the following types based on the VXLAN tunnel creation mode:
  Static tunnel: You need to manually configure local and remote VNIs, VTEP IP addresses, and ingress replication list.
  Dynamic tunnel: VXLAN tunnels are dynamically established using BGP Ethernet Virtual Private Network (Ethernet VPN). When BGP EVPN is used to dynamically establish a VXLAN tunnel, the local and remote VTEPs first establish a BGP EVPN peer relationship before exchanging BGP EVPN routes to learn the VNIs and VTEP IP addresses from each other.
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning

## Slide 26: Static VXLAN Tunnel
A static VXLAN tunnel is not a stateful tunnel (for example, an IPsec VPN tunnel). It is similar to a GRE VPN tunnel for data transmission.
The address in the ingress replication list is the tunnel destination address that is encapsulated when VXLAN packets are encapsulated and transmitted over the VXLAN tunnel.
VTEP1
1.1.1.1/32
VTEP2
2.2.2.2/32
VTEP3
3.3.3.3/32
PC1
172.16.1.1/24
PC2
172.16.2.2/24
PC3
172.16.1.3/24
PC4
172.16.2.4/24
BD 10
VNI 100
BD 20
VNI 200
BD 10
VNI 100
BD 20
VNI 200
interface nve 1
source 1.1.1.1
vni 100 head-end peer-list 3.3.3.3
vni 200 head-end peer-list 2.2.2.2
interface nve 1
source 2.2.2.2
vni 200 head-end peer-list 1.1.1.1
interface nve 1
source 3.3.3.3
vni 100 head-end peer-list 1.1.1.1
VXLAN tunnel
VXLAN tunnel
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning

## Slide 27: VXLAN MAC Address Entries
VXLAN implements Layer 2 forwarding on the overlay network. Unicast data frames are forwarded based on MAC address entries.
When a VTEP receives a data frame from the local device in a BD, the VTEP adds the source MAC address of the data frame to the MAC address table of the BD and sets the outbound interface to the interface that receives the data frame.
This entry is used to guide the forwarding of data frames sent to a device connected to the VTEP.
PC1
172.16.1.1/24
0000-0000-000A
PC2
172.16.2.2/24
0000-0000-000B
BD 10
VNI 100
BD 20
VNI 200
GE1/0/1.10
GE1/0/1.20
<S1>display mac-address bridge-domain 10
-------------------------------------------------------------------------------
MAC Address VLAN/VSI/BD Learned-From Type
-------------------------------------------------------------------------------
0000-0000-000a -/-/10 GE1/0/1.10 dynamic
<S1>display mac-address bridge-domain 20
-------------------------------------------------------------------------------
MAC Address VLAN/VSI/BD Learned-From Type
-------------------------------------------------------------------------------
0000-0000-000b -/-/20 GE1/0/1.20 dynamic
How are data frames forwarded to a device connected to a remote VTEP?
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning

## Slide 28: Dynamic MAC Address Learning (1)
Before forwarding data frames of a device connected to a remote VTEP, the local VTEP needs to learn the MAC address of the remote VTEP.
This process is similar to the traditional MAC address table generation process and depends on packet exchange between hosts. Generally, MAC address entries are generated through ARP packet exchange.
SW1 (Layer 2 gateway)
VTEP 1.1.1.1/32
SW2 (Layer 2 gateway)
VTEP 2.2.2.2/32
VXLAN tunnel (VNI 1000)
PC1
192.168.1.1/24
0000-0000-000A
PC2
192.168.1.2/24
0000-0000-000B
ARP packet
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
ARP packet
Ethernet header
1
3
5
MAC Address | BD | Learned From
0000-0000-000A | 10 | Port1
MAC Address | BD | Learned From
0000-0000-000A | 10 | 1.1.1.1
2
4
PC1 broadcasts an ARP Request packet.
SW1 learns the MAC address of PC1.
SW2 learns the MAC address of PC1.
SW2 forwards the ARP packet to PC2.
Port1
Port1
SW1 performs VXLAN encapsulation for the ARP packet, and floods the VXLAN-encapsulated ARP packet to all VTEPs.
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning
Notes: Communication between PC1 and PC2 is as follows:
  To communicate with PC2, PC1 broadcasts an ARP Request packet to obtain the MAC address of PC2.
  After receiving the packet, SW1 determines the BD ID, destination VXLAN tunnel, and VNI of the traffic based on VAP information. In addition, SW1 learns the MAC address of PC1 and records the BD ID and the interface that receives the packet in the corresponding MAC address entry.
  SW1 performs VXLAN encapsulation for the ARP Request packet and forwards the encapsulated packet based on the ingress replication list.
  After receiving the VXLAN packet, SW2 decapsulates the packet to obtain the original data frame. In addition, SW2 learns the MAC address of PC1 and records the BD ID and the VTEP address of SW1 in the corresponding MAC address entry.
  SW2 floods the ARP packet in the local BD. PC2 then receives the packet and learns the ARP information of PC1.

## Slide 29: Dynamic MAC Address Learning (2)
SW1 (Layer 2 gateway)
VTEP 1.1.1.1/32
SW2 (Layer 2 gateway)
VTEP 2.2.2.2/32
VXLAN tunnel (VNI 1000)
PC1
172.16.1.1/24
0000-0000-000A
PC2
172.16.1.2/24
0000-0000-000B
ARP packet
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
ARP packet
Ethernet header
10
8
6
MAC Address | BD | Learned From
0000-0000-000A | 10 | Port1
0000-0000-000B | 10 | 2.2.2.2
MAC Address | BD | Learned From
0000-0000-000A | 10 | 1.1.1.1
0000-0000-000B | 10 | Port1
9
7
SW1 forwards the ARP packet to PC1.
SW1 learns the MAC address of PC2.
SW2 learns the MAC address of PC2.
PC2 sends a unicast ARP Reply packet.
Port1
Port1
SW2 searches the MAC address table, encapsulates the ARP packet according to the MAC address entry {0000-0000-000A, 10, 1.1.1.1}, and sends the packet to 1.1.1.1.
PC1 and PC2 have learned ARP entries of each other, and SW1 and SW2 have learned MAC addresses of PC1 and PC2. This process is called flood and learn.
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning
Notes:   PC2 sends a unicast ARP Reply packet.
  SW2 has the MAC address entry of PC1; therefore, SW2 unicasts the packet and learns the source MAC address of PC2 in the MAC address entry.
  SW2 encapsulates the ARP Reply packet with a VXLAN header and sends it to the remote VTEP at 1.1.1.1.
  After SW1 receives the VXLAN packet, it decapsulates the packet and records the source MAC address of PC2 in the MAC address table. The outbound interface is the remote VTEP.
  SW1 forwards the packet to PC1.
By doing this, PC1 and PC2 learn ARP entries of each other, and SW1 and SW2 learn MAC addresses of each other.

## Slide 30: Intra-Subnet Forwarding of Unicast Packets with Known Destination Addresses
SW1 (Layer 2 gateway)
VTEP 1.1.1.1/32
SW2 (Layer 2 gateway)
VTEP 2.2.2.2/32
VXLAN tunnel (VNI 1000)
PC1
192.168.1.1/24
AAAA-0000-0001
PC2
192.168.1.2/24
AAAA-0000-0002
MAC Address | BD | Learned From
AAAA-0000-0001 | 10 | Port1
AAAA-0000-0002 | 10 | 2.2.2.2
MAC Address | BD | Learned From
AAAA-0000-0001 | 10 | 1.1.1.1
AAAA-0000-0002 | 10 | Port1
2
4
Port1
Port1
SW1 searches its MAC address table for the MAC address of PC2 and finds the matching entry.
SW2 searches its MAC address table for the MAC address of PC2 and finds the matching entry.
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
Payload
Ethernet header
1
3
5
PC1 sends a unicast frame to PC2.
SW1 performs VXLAN encapsulation for the packet and adds a new IP header to the packet. The destination IP address of the packet is 2.2.2.2, which is the IP address of the remote VTEP SW2.
SW2 forwards the packet to PC2.
Source IP address: 1.1.1.1
Destination IP address: 2.2.2.2
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning

## Slide 31: BUM Traffic Forwarding
When transmitting broadcast, unknown, and multicast (BUM) traffic, the VTEP replicates the traffic and sends multiple copies to the remote VTEP in the ingress replication list. In this way, BUM traffic is flooded on the overlay network.
BUM traffic
VTEP1
1.1.1.1/32
VTEP2
2.2.2.2/32
VTEP3
3.3.3.3/32
PC1
172.16.2.1/24
PC2
172.16.2.2/24
PC3
172.16.2.3/24
BD 20
VNI 200
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VXLAN tunnel
1
2
Replication and encapsulation
BUM traffic
VXLAN header
UDP
IP Src 1.1.1.1, IP Dst 2.2.2.2
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning

## Slide 32: Inter-Subnet Forwarding
PC1 192.168.1.1/24
Default gateway: 192.168.1.254
Server2 192.168.2.1/24
Default gateway: 192.168.2.254
BD 10 (VNI 1000)
BD 20 (VNI 2000)
VBDIF 10
192.168.1.254
00AB-09FF-1111
VBDIF 20
192.168.2.254
00AB-09FF-2222
SW1
Layer 2 gateway
SW2
Layer 2 gateway
SW3
Layer 3 gateway
Destination/Mask | Outbound Interface | Next Hop
192.168.1.0/24 | VBDIF10 | 192.168.1.254
192.168.2.0/24 | VBDIF20 | 192.168.2.254
VTEP 1.1.1.1/32
VTEP 2.2.2.2/32
VTEP 3.3.3.3/32
1
2
4
5
Routing table of SW3
3
Payload
Ethernet header
Payload
Ethernet header
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
Source IP address: 1.1.1.1
Destination IP address: 3.3.3.3
VNI: 1000
Original data frame
VXLAN header
UDP header
IP header
Ethernet header
Source IP address: 3.3.3.3
Destination IP address: 2.2.2.2
VNI: 2000
PC1 sends a unicast frame to PC2.
Tunnel Establishment
Data Frame Forwarding
MAC Address Learning
Notes: PC1 wants to communicate with Server2. When finding that Server2 is on a different subnet, PC1 sends the packet to the gateway.
PC1 sends a data packet to Server2. The destination MAC address of the data packet is 00AB-09FF-1111 (gateway MAC address). After receiving the data packet, SW1 searches the Layer 2 forwarding table and finds that the outbound interface is a remote VTEP (Layer 3 gateway). Therefore, SW1 adds a VXLAN header (VNI = 1000) to the data packet. Then the packet is sent to SW3.
After receiving the packet, SW3 decapsulates the VXLAN packet and finds that the destination MAC address of the internal original data packet is 00AB-09FF-1111, which is the MAC address of its own interface VBDIF10. Then SW3 needs to search the Layer 3 forwarding table.
SW3 searches the routing table and finds that the destination IP address 192.168.2.1 matches the direct route generated by VBDIF 20. SW3 then searches the ARP table for the destination MAC address of the packet and searches the MAC address table for the outbound interface of the packet. On SW3, the outbound interface for the MAC address corresponding to 192.168.2.1 is the remote VTEP at 2.2.2.2. SW3 encapsulates the packet into a VXLAN packet and sends it to SW2.
After receiving the packet, SW2 decapsulates the VXLAN packet and finds that the destination MAC address is not the MAC address of any local interface. SW2 then searches the Layer 2 forwarding table and forwards the packet through the local interface based on the MAC address table.

## Slide 33
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
  Basic Concepts
  Fundamentals
  Basic Configuration
BGP EVPN
Campus Network Virtualization

## Slide 34: VXLAN Configuration (1)
[Huawei] bridge-domain bd-id
Create a BD.
Create a BD in the system view and enter the BD view. The value ranges from 1 to 16777215.
[Huawei-bd100] vxlan vni vni-id
Create a VNI.
Create a VNI in the BD view and associate the VNI with the BD. The value ranges from 1 to 16777215.
[Huawei] interface nve nve-number
Create an NVE interface.
Create an NVE interface and enter its view. The NVE interface number must be 1.
[Huawei-Nve1] source ip-address
4. Configure an IP address for the source VTEP.
Configure an IP address for the source VTEP. A loopback interface's address is recommended.

## Slide 35: VXLAN Configuration (2)
[Huawei-Nve1] vni vni-id head-end peer-list ip-address &<1-10>
Configure an ingress replication list.
Configure a VNI in the NVE view and specify the IP addresses of multiple remote VTEPs to create an ingress replication list. The local NVE replicates and forwards packets based on the list.
[Huawei-GE1/0/1.1] encapsulation { dot1q [ vid low-vid [ to high-vid ] ] | default | untag | qinq [ vid id ]}
Configure an encapsulation mode on a sub-interface.
Configure an encapsulation mode to determine the type of data packet that can pass through the Layer 2 sub-interface.
[Huawei-bd] l2 binding vlan vlan-id
Bind a VLAN to the BD.
This command is configured in the BD view. Before binding a global VLAN to a BD, ensure that the global VLAN has been created and interfaces have been added to the global VLAN.
[Huawei] interface vbdif bd-id
Configure a Layer 3 gateway.
Create a VBDIF interface in the system view, enter the VBDIF interface view, and configure a gateway IP address in the VBDIF interface view.

## Slide 36: Configuration Example: Intra-Subnet Communication (1)
IP1
192.168.1.1/24
IP2
192.168.1.2/24
IP3
192.168.1.3/24
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
GE1/0/10
GE1/0/1
GE1/0/2
GE1/0/1
BD 100
VNI 10000
SW1
SW2
[SW1] bridge-domain 100
[SW1-bd100] vxlan vni 10000
[SW1] interface Nve 1
[SW1-Nve1] source 1.1.1.1
[SW1-Nve1]vni 10000 head-end peer-list 2.2.2.2
SW1 configuration:
Configure a VXLAN tunnel
Configure service access
SW2 configuration:
[SW2] bridge-domain 100
[SW2-bd100] vxlan vni 10000
[SW2] interface Nve 1
[SW2-Nve1] source 2.2.2.2
[SW2-Nve1]vni 10000 head-end peer-list 1.1.1.1
Configure a VXLAN tunnel between the two switches to enable the three PCs on the same network segment to communicate with each other.

## Slide 37: Configuration Example: Intra-Subnet Communication (2)
SW1 configuration:
SW2 configuration:
Configure a VXLAN tunnel between the two switches to enable the three PCs on the same network segment to communicate with each other.
[SW1]interface GigabitEthernet 1/0/1.1 mode l2
[SW1-GigabitEthernet1/0/1.1]encapsulation untag
[SW1-GigabitEthernet1/0/1.1]bridge-domain 100
[SW1]interface GigabitEthernet 1/0/2.1 mode l2
[SW1-GigabitEthernet1/0/2.1]encapsulation untag
[SW1-GigabitEthernet1/0/2.1]bridge-domain 100
[SW2] bridge-domain 100
[SW1-bd100] l2 binding vlan 1
Question 1: What is the difference between access modes of SW2 and SW1?
Question 2: How is the gateway 192.168.1.254 configured?
IP1
192.168.1.1/24
IP2
192.168.1.2/24
IP3
192.168.1.3/24
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
GE1/0/10
GE1/0/1
GE1/0/2
GE1/0/1
BD 100
VNI 10000
SW1
SW2
Configure a VXLAN tunnel
Configure service access
Notes: SW1 provides Layer 2 sub-interface access, and SW2 uses the VLAN binding mode.
Create a VBDIF interface as the gateway for terminals in the BD.

## Slide 38: Configuration Example: Inter-subnet Communication (Centralized Gateway) (1)
192.168.1.10/24
192.168.2.10/24
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
GE1/0/1
SW1
SW2
GE1/0/1
SW3
VTEP
3.3.3.3/32
BD 100
VNI 10000
192.168.1.1
BD 200
VNI 20000
192.168.2.1
VXLAN tunnels are configured between the three switches to implement mutual access between two PCs on different network segments. The centralized VXLAN gateway is deployed on SW3.
[SW1] bridge-domain 100
[SW1-bd100] vxlan vni 10000
[SW1] interface Nve 1
[SW1-Nve1] source 1.1.1.1
[SW1-Nve1]vni 10000 head-end peer-list 3.3.3.3
SW1 configuration:
SW2 configuration:
[SW2] bridge-domain 200
[SW2-bd100] vxlan vni 20000
[SW2] interface Nve 1
[SW2-Nve1] source 2.2.2.2
[SW2-Nve1] vni 20000 head-end peer-list 3.3.3.3
Configure a VXLAN tunnel
Configure service access
Configure a gateway
Question: How is SW3 configured?
Notes: On SW3, configure NVE interfaces to connect to SW1 and SW2, and create VBDIF 100 and VBDIF 200 as gateways of terminals in BD 100 and BD 200.

## Slide 39: Configuration Example: Inter-subnet Communication (Centralized Gateway) (2)
192.168.1.10/24
192.168.2.10/24
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
GE1/0/1
SW1
SW2
GE1/0/1
SW3
VTEP
3.3.3.3/32
BD 100
VNI 10000
192.168.1.1
BD 200
VNI 20000
192.168.2.1
[SW1] interface GigabitEthernet 1/0/1.1 mode l2
[SW1-GigabitEthernet1/0/1.1] encapsulation untag
[SW1-GigabitEthernet1/0/1.1] bridge-domain 100
SW1 configuration:
SW2 configuration:
[SW1] interface GigabitEthernet 1/0/1.1 mode l2
[SW1-GigabitEthernet1/0/1.1] encapsulation untag
[SW1-GigabitEthernet1/0/1.1] bridge-domain 200
If traffic from 192.168.2.10 carries VLAN 20, how do we configure SW2?
Configure a VXLAN tunnel
Configure service access
Configure a gateway
VXLAN tunnels are configured between the three switches to implement mutual access between two PCs on different network segments. The centralized VXLAN gateway is deployed on SW3.
Notes: Configure GE1/0/1 of SW2 as a trunk interface to allow packets from VLAN 20 to pass through (you can also configure the interface as an access interface and the default VLAN as VLAN 20), and bind VLAN 20 to BD 200.

## Slide 40: Configuration Example: Inter-subnet Communication (Centralized Gateway) (3)
192.168.1.10/24
192.168.2.10/24
VTEP
1.1.1.1/32
VTEP
2.2.2.2/32
GE1/0/1
SW1
SW2
GE1/0/1
SW3
VTEP
3.3.3.3/32
BD 100
VNI 10000
192.168.1.1
BD 200
VNI 20000
192.168.2.1
SW3 configuration:
VXLAN
VXLAN
Configure a VXLAN tunnel
Configure service access
Configure a gateway
[SW3] interface Vbdif100
[SW3-Vbdif100] ip address 192.168.1.1 24
[SW3] interface Vbdif200
[SW3-Vbdif200] ip address 192.168.2.1 24
[SW3] bridge-domain 100
[SW3-bd100] vxlan vni 10000
[SW3] interface Nve 1
[SW3-Nve1] source 3.3.3.3
[SW3-Nve1]vni 10000 head-end peer-list 1.1.1.1
[SW3-Nve1]vni 20000 head-end peer-list 2.2.2.2
[SW3] bridge-domain 200
[SW3-bd200] vxlan vni 20000
VXLAN tunnels are configured between the three switches to implement mutual access between two PCs on different network segments. The centralized VXLAN gateway is deployed on SW3.

## Slide 41
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
BGP EVPN
  Basic Concepts
  BGP EVPN Routes
  BGP EVPN Features
Campus Network Virtualization

## Slide 42: Using BGP EVPN as the Control Plane Protocol
BGP EVPN not used
BGP EVPN used as the control plane protocol
Problem 1: A total of N x (N-1)/2 tunnels need to be created for N nodes, causing heavy configuration workload.
Problem 2: The flood and learn mechanism is used to learn MAC addresses. As a result, a large amount of traffic is flooded.
VXLAN tunnel
Traffic flooding
BGP EVPN
peer relationship
Route reflector (RR)
BGP EVPN is enabled on devices. BGP EVPN peer relationships are established between devices.
Devices exchange BGP EVPN routes to complete VXLAN control plane operations.
VXLAN tunnels are automatically established through BGP EVPN, and forwarding entries are dynamically updated through BGP EVPN.
In practice, RRs can be used to further reduce the number of BGP EVPN peer relationships.
Notes: The static VXLAN solution does not have a control plane. VTEP discovery and learning of host information (including IP addresses, MAC addresses, VNIs, and gateway VTEP IP addresses) are performed through traffic flooding on the data plane. As a result, there is a lot of flooded traffic on VXLAN networks. To address this problem, VXLAN uses EVPN as the control plane protocol. EVPN allows VTEPs to exchange BGP EVPN routes to implement automatic VTEP discovery and host information advertisement, preventing unnecessary traffic flooding.
Problems in configuring VXLAN in static mode:
  If N devices need to establish VXLAN tunnels, you need to manually configure the ingress replication list a maximum of N(N-1)/2 times.
  A static VXLAN tunnel only has the data forwarding plane.
  Remote MAC addresses can be learned only through broadcast ARP packets.

## Slide 43: Overview of BGP EVPN
EVPN extends BGP to define several types of BGP EVPN routes (the MP_REACH_NLRI attribute defines several new NLRIs, which are called EVPN NLRIs).
The BGP EVPN routes can be used to transmit VTEP addresses and host information. EVPN is applied to VXLAN networks to move VTEP discovery and host information learning from the data plane to the control plane.
SW1
SW2
BGP EVPN peer relationship
Type 2 routes (MAC/IP routes): are used to advertise host MAC addresses, ARP entries, and IP routes.
Type 3 routes (inclusive multicast routes): are used to transmit Layer 2 VNI (L2VNI) and VTEP IP address information, implement automatic VTEP discovery, dynamic VXLAN tunnel establishment, and BUM packet forwarding.
Type 5 routes (IP prefix routes): are used to advertise host MAC addresses, ARP entries, IP routes, and external network routes.
Notes: In a network virtualization overlay (NVO) scenario, BGP EVPN is used together with VXLAN as the control plane protocol for VXLAN.

## Slide 44: EVPN NLRI
EVPN NLRI is carried in the path attribute MP_REACH_NLRI. The address family identifier (AFI) is 25, indicating L2VPN; the sub-address family identifier (SAFI) is 70.
Path Attribute - MP_REACH_NLRI
Flags: Optional, Non-transitive
Type Code: MP_REACH_NLRI (14)
Length
Address family identifier (AFI): Layer-2 VPN (25)
Subsequent address family identifier (SAFI): EVPN (70)
Next hop network address (4 Bytes)
Route Type (1 octet)
Length (1 octet)
Route Type specific (variable)
EVPN NLRI

## Slide 45: Extended Community
BGP EVPN is similar to MPLS VPN. To control the sending and receiving of routes, BGP EVPN uses the EVPN instance, which is the same as the traditional IP VPN instance. An EVPN instance has RD and RT values. When routes are transmitted, the extended community attribute is used to carry the RT value of the EVPN instance.
In addition to the RT value, BGP EVPN adds some new sub-types to the extended community attribute: MAC Mobility and EVPN Router's MAC Extended Community.
Path Attribute - EXTENDED_COMMUNITIES
Flags: Optional, Transitive
Type Code: EXTENDED_COMMUNITIES (16)
Length
Route Target (RT)
MAC Mobility
EVPN Router's MAC Extended Community
Extended Community
Notes: For details about the RD and RT, see the HCIP-Advanced Routing Switching - 08 MPLS VPN Principles and Configuration.

## Slide 46: EVPN VPN Instance
After an EVPN instance is bound to a BD, MAC address entries of the BD are transmitted through BGP EVPN routes, carrying the ERT of the EVPN instance bound to the BD. After receiving the EVPN routes, the remote end compares the ERT carried in the EVPN routes with the IRT of the local EVPN instance and adds the EVPN routes to the routing table of the EVPN instance. The remote end parses the EVPN routing table to obtain MAC address entries and adds them to the MAC address table of the BD bound to the EVPN instance.
SW1
VTEP 1.1.1.1/32
SW2
VTEP 2.2.2.2/32
VXLAN tunnel
PC1
EVPN RD: 20:1
EVPN ERT: 202:1
EVPN IRT: 200:1
BD 20
VNI 200
EVPN instance e1
BD 20
VNI 200
EVPN instance e1
EVPN RD: 20:1
EVPN ERT: 200:1
EVPN IRT: 202:1
PC2
If the ERT and IRT values are not specified and only the RT value is available, the ERT and IRT values are the same.
BGP Update message
EVPN route
EVPN RT = 202:1

## Slide 47
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
BGP EVPN
  Basic Concepts
  BGP EVPN Routes
  BGP EVPN Features
Campus Network Virtualization

## Slide 48: MAC/IP Route (1)
Type 2 routes (MAC/IP routes): are used to advertise host MAC addresses, ARP entries, and IP routes.
Route Distinguisher (8 bytes)
Ethernet Segment Identifier (10 bytes)
Ethernet Tag ID (4 bytes)
MAC Address Length (1 byte)
MAC Address (6 bytes)
IP Address Length (1 byte)
IP Address (0, 4, or 16 bytes)
MPLS Label1 (3 bytes)
MPLS Label2 (0 or 3 bytes)
Route distinguisher (RD) of an EVPN instance.
Unique ID for defining the connection between local and remote devices.
VLAN ID configured on the device.
Length of the host MAC address carried in the route.
Host MAC address carried in the route.
Mask length of the host IP address carried in the route
Host IP address carried in the route.
L2VNI carried in the route.
L3VNI carried in the route.
Format of a MAC/IP route
Field description
Type 2 Route
Type 5 Route
Type 3 Route

## Slide 49: MAC/IP Route (2)
In different scenarios, Type 2 routes carry different contents.
MAC address advertisement
ARP advertisement
IP route advertisement
Route Distinguisher
Ethernet Segment Identifier
Ethernet Tag ID
MAC Address Length
MAC Address
IP Address Length
IP Address
MPLS Label1 = L2VNI
MPLS Label2
Route Distinguisher
Ethernet Segment Identifier
Ethernet Tag ID
MAC Address Length
MAC Address
IP Address Length
IP Address
MPLS Label1 = L2VNI
MPLS Label2
Route Distinguisher
Ethernet Segment Identifier
Ethernet Tag ID
MAC Address Length
MAC Address
IP Address Length
IP Address
MPLS Label1 = L2VNI
MPLS Label2 = L2VNI
When hosts on the same subnet communicate with each other, the host MAC address is advertised, including the host MAC address and L2VNI.
In a centralized gateway scenario, ARP routes are advertised, including host IP addresses, MAC addresses, and L2VNIs.
IRB routes are advertised when inter-subnet mutual access is deployed in a distributed gateway scenario. The routes carry MAC addresses, IP addresses, L2VNIs, and L3VNIs of hosts.
Type 2 Route
Type 5 Route
Type 3 Route
Notes: The first three fields (RD, Ethernet Segment Identifier, and Ethernet Tag ID) of a Type 2 route are the same in different scenarios, and only the last six fields are different.

## Slide 50: MAC Address Advertisement
This slide shows how BGP EVPN uses Type 2 routes to implement dynamic MAC address learning. This function is used to implement intra-subnet communication through VXLAN.
SW1 (Layer 2 gateway)
VTEP 1.1.1.1/32
SW2 (Layer 2 gateway)
VTEP 2.2.2.2/32
VXLAN tunnel
MAC Address | BD | Learned From
0000-0000-0001 | 10 | Port1
PC1 172.16.1.1/24
0000-0000-0001
PC2
MAC Address | BD | Learned From
0000-0000-0001 | 10 | 1.1.1.1
2
3
Send traffic
1
Learn the MAC address of PC1
4
BD 10
L2 VNI 10
RD 10:1
ERT 10:1
BD 10
L2 VNI 10
RD 20:1
IRT 10:1
BGP Update message
Type 2 route
RD = 10:1
MAC address = 0000-0000-0001
VNI = 10
EVPN RT = 10:1
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: Intra-subnet host MAC address advertisement:
  PC1 generates data traffic and sends the traffic to SW1.
  SW1 obtains the MAC address of PC1 and creates an entry in the MAC address table to record the MAC address, BD ID, and inbound interface.
  SW1 generates a BGP EVPN route based on this entry and sends the route to SW2. The route carries the RT value of the local EVPN instance and Type 2 route (MAC route). In the MAC route, the MAC address of PC1 is stored in the MAC Address field and the L2VNI is stored in the MPLS Label1 field.
  After receiving the BGP EVPN route from SW1, SW2 checks the RT (similar to the RT concept in MPLS VPN) carried in the route. If the RT is the same as the import RT of the local EVPN instance, SW2 accepts the route. Otherwise, SW2 discards the route. After accepting the route, SW2 obtains the MAC address of PC1 and the mapping between the BD ID and the VTEP IP address (next hop network address in MP_REACH_NLRI) of SW1, and generates the MAC address entry of PC1 in the local MAC address table. Based on the next hop, the outbound interface of the MAC address entry recurses to the VXLAN tunnel destined for SW1.

## Slide 51: ARP Advertisement
This slide describes how BGP EVPN uses Type 2 routes to advertise host ARP entries.
SW1 (Layer 3 gateway)
VTEP 1.1.1.1/32
SW2 (Layer 3 gateway)
VTEP 2.2.2.2/32
VXLAN tunnel
PC1 172.16.1.1/24
0000-0000-0001
1
SW1 learns the ARP entry of PC1.
2
3
The Layer 3 gateway SW2 obtains ARP information of PC1.
When BGP EVPN is used in a centralized gateway scenario, the inter-subnet packet forwarding process is similar to that in a static VXLAN scenario.
BD 10
L2 VNI 10
RD 10:1
ERT 10:1
BD 10
L2 VNI 10
RD 20:1
IRT 10:1
BGP Update message
Type 2 route
RD = 10:1
MAC address =0000-0000-0001
IP address = 172.16.1.1
L2VNI = 10
EVPN RT = 10:1
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: A MAC/IP route can carry both the MAC and IP addresses of a host, and therefore can be used to advertise ARP entries between VTEPs. The MAC Address and MAC Address Length fields identify the MAC address of the host, whereas the IP Address and IP Address Length fields identify the IP address of the host. This type of MAC/IP route is called the ARP route. ARP advertisement applies to the following scenarios:
  ARP broadcast suppression. After a Layer 3 gateway learns the ARP entries of a host, it generates host information that contains the host IP and MAC addresses, Layer 2 VNI, and gateway's VTEP IP address. The Layer 3 gateway then transmits an ARP route carrying the host information to a Layer 2 gateway. When the Layer 2 gateway receives an ARP request, it checks whether it has the host information corresponding to the destination IP address of the packet. If such host information exists, the Layer 2 gateway replaces the broadcast MAC address in the ARP request with the destination unicast MAC address and unicasts the packet. This implementation suppresses ARP broadcast packets.
  VM migration in distributed gateway scenarios. After a VM migrates from one gateway to another, the new gateway learns the ARP entry of the VM (after the VM sends gratuitous ARP packets) and generates host information that contains the host IP and MAC addresses, Layer 2 VNI, and gateway's VTEP IP address. The new gateway then transmits an ARP route carrying the host information to the original gateway. After the original gateway receives the ARP route, it detects a VM location change and triggers ARP probe. If ARP probe fails, the original gateway withdraws the ARP and host routes of the VM.
ARP advertisement is mainly used in the centralized VXLAN gateway+BGP EVPN scenario. In BGP EVPN, ARP or IRB advertisement to peers is mutually exclusive. Only one of these routes can be configured to advertise. Generally, ARP advertisement is selected in the centralized VXLAN gateway+BGP EVPN scenario, in the distributed VXLAN gateway+BGP EVPN scenario, IRB routes are advertised.

## Slide 52: Inter-Subnet Communication in a Distributed Gateway Scenario
VTEP1
PC1
172.16.2.1/24
PC2
172.16.1.2/24
BD 20
VNI 200
BD 10
VNI 100
VXLAN tunnel
VTEP2
VBDIF 10
VBDIF 20
VBDIF 10
VBDIF 20
In distributed gateway networking, VBDIF 10 and VBDIF 20 can be created on both VTEP1 and VTEP2. How do we implement routing between VBDIF interfaces during inter-subnet communication?
Inter-subnet forwarding in a VLAN through a VLANIF interface
Inter-BD forwarding in a VLAN through a VLANIF interface
VLANIF 20
VLANIF 10
PC1
172.16.10.1/24
MAC 1
VLAN 10
PC2
172.16.20.2/24
MAC 3
VLAN 20
Bridge
1
Bridge
3
Routing
2
MAC 2
MAC 2
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: In distributed gateway networking, VTEPs function as both Layer 2 and Layer 3 gateways. In this networking, inter-subnet communication is implemented in multiple modes. According to the processing mode of ingress VTEPs, inter-subnet communication can be implemented through asymmetric and symmetric Integrated Routing and Bridging (IRB).
Inter-subnet forwarding in a VLAN through a VLANIF interface:
  Based on the local IP address, local mask, and peer IP address, PC1 finds that the destination device PC2 is on a different network segment from itself. Therefore, PC1 determines Layer 3 communication and sends the traffic destined for PC2 to the gateway. In the data packet sent by PC1, the source MAC address is MAC1 and the destination MAC address is MAC2.
  After receiving the packet sent from PC1 to PC2, the switch decapsulates the packet and finds that the destination MAC address is the MAC address of VLANIF 10. Therefore, the switch considers that the packet is sent to itself and sends the packet to the routing module for further processing.
  The routing module parses the packet and finds that the destination IP address is 192.168.20.2, which is not the IP address of the local interface. Therefore, the routing module needs to forward the packet at Layer 3. When the routing module searches the routing table, it matches the direct route generated by VLANIF 20 against the packet.

## Slide 53
Notes:   Because the direct route is matched, the packet has reached the last hop. Therefore, the switch searches the ARP table for 192.168.20.2, obtains the MAC address corresponding to 192.168.20.2, and sends the packet to the switching module to re-encapsulate the packet into a data packet.
  The switching module searches the MAC address table to determine the outbound interface of the packet and whether the packet needs to carry a VLAN tag. In the data packet sent by the switching module, the source MAC address is MAC2, the destination MAC address is MAC3, and the VLAN tag is None.
In the preceding forwarding process, the switch determines whether the packet is forwarded at Layer 3 based on the destination MAC address of the data packet. If the destination MAC address is the MAC address of the switch, the switch forwards the packet based on the Layer 3 forwarding table. Otherwise, the switch forwards the packet based on the Layer 2 forwarding table. This process is involved in both symmetric and asymmetric IRB scenarios.
Ingress VTEP: VTEP through which traffic enters a VXLAN network.
Egress VTEP: VTEP through which traffic goes out of a VXLAN network.

## Slide 54: Asymmetric IRB
Asymmetric IRB: The ingress VTEP performs both Layer 3 and Layer 2 table lookup, and the egress VTEP only needs to perform Layer 2 table lookup and forwarding. This is called asymmetric forwarding because the operations performed by the ingress VTEP and egress VTEP are different.
PC1
172.16.2.1/24
MAC A
PC2
172.16.1.2/24
MAC B
BD 20
VNI 200
BD 10
VNI 100
VXLAN tunnel
BD 20
VNI 200
BD 10
VNI 100
1
PC1 sends a unicast packet to PC2.
2
VBDIF 20 searches the routing table
and sends the packet to VBDIF 10.
3
VBDIF 10 queries the MAC address table of BD 10 and finds that the destination MAC address (learned through a Type 2 route) is that of the remote VTEP.
4
VTEP1 sends the data packet to VTEP2 through the VXLAN tunnel.
BD 10
VNI 100
5
VTEP2 searches the Layer 2 table in BD 10 corresponding to VNI 100.
6
VTEP2 sends the data packet to PC2.
VBDIF 10
VBDIF 20
VBDIF 10
VBDIF 20
VTEP1
1.1.1.1
VTEP2
2.2.2.2
Outer IP
UDP
VXLAN header (VNI 100)
Source MAC: MAC address of VBDIF 10 Destination MAC: MAC B
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: During asymmetric IRB, VTEPs do not transmit host IP routes between each other. That is, VTEP1 and VTEP2 do not transmit the 32-bit host route (generated through an ARP entry) of the connected PC. Therefore, VTEP1 searches the routing table in step 2, and matches the packet against the direct route generated by VBDIF 10.
In step 5, VTEP2 decapsulates the VXLAN packet and finds that the destination MAC address is not the MAC address of the local VBDIF interface corresponding to the BD. Therefore, VTEP2 searches the Layer 2 forwarding table for the MAC address entry of the corresponding BD based on the VNI carried in the packet and then forwards the packet at Layer 2.

## Slide 55: Symmetric IRB
Symmetric IRB: Both the ingress and egress VTEPs perform Layer 3 table lookup and forwarding.
Compared with asymmetric IRB, symmetric IRB adds an IP VPN instance and its bound L3VNI. In asymmetric IRB mode, the VNI in the VXLAN header of packets transmitted between VTEPs is the L2VNI. The VBDIF interface needs to be bound to an IP VPN instance. In this case, route learning and data forwarding are restricted to the IP VPN instance, which is similar to MPLS VPN.
IP VPN-Instance VPN1
VXLAN VNI 1000 (L3VNI)
RD 203:1
RT 10:1
VBDIF 20
IP Bind VPN-Instance VPN1
BD 20
VTEP1
1.1.1.1
VXLAN tunnel
VTEP2
2.2.2.2
IP VPN-Instance VPN1
VXLAN VNI 1000 (L3VNI)
RD 103:1
RT 10:1
VBDIF 10
IP Bind VPN-Instance VPN1
BD 10
In this case, IRB routes (additional L3VNI) are transmitted between VTEPs. The learning of IRB routes between BD 20 of VTEP1 and BD 10 of VTEP2 is controlled by the RT values carried in the routes. This mechanism is similar to the MPLS VPN VPNv4 route learning mechanism.
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: On Huawei devices, Symmetric IRB is used.

## Slide 56: EVPN RT and IP VPN RT (1)
After an IP VPN instance is added, the RT value carried in the Type 2 route transmitted by BGP EVPN is still the EVPN RT value. The only difference is that the remote end processes the received route differently.
  If the RT carried in the route is the same as the IRT of the local EVPN instance, the route is accepted. After the EVPN instance obtains IRB routes, it can extract ARP routes from the IRB routes to implement ARP advertisement.
  If the RT carried in the route is the same as the IRT of the local EVPN instance, the route is accepted. Then, the L3VPN instance obtains the IP prefix type route carried in the route, extracts the host IP address and L3VNI, and saves the host IP route of Host1 to the routing table. The outbound interface is recursed based on the next hop of the route and is the VXLAN tunnel to the VTEP.
Type 2 Route
Type 5 Route
Type 3 Route
MAC address advertisement
ARP advertisement
IP route advertisement
Notes: In a BGP EVPN scenario, if you want to control the sending and receiving of EVPN routes based on the RT value of the IP VPN instance, run the vpn-target evpn command to configure the RT value. In this case, the ERT is carried in EVPN routes and sent to the remote BGP EVPN peer, the IRT matches the RT carried in an EVPN route to determine which EVPN routes can be added to the routing table of the local VPN instance address family.
Note: The RT configured using the vpn-target evpn command is called an RT (EVPN), which is different from common RTs.

## Slide 57: EVPN RT and IP VPN RT (2)
A route is discarded only when its RT is different from the EVPN IRT and IP VPN IRT (EVPN).
BGP Update message
EVPN route
EVPN RT = 20:1
VTEP2
VTEP1
BD 20
EVPN ERT 20:1
BD 20
EVPN IRT 20:1
VBDIF 20
IP VPN IRT 20:1
BGP EVPN routing table
IP VPN routing table
EVPN route
1
3
Host IP route
EVPN route
The RT carried in the route is the same as the IRT of the IP VPN instance.
2
The RT carried in the route is the same as the IRT of the EVPN instance.
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: VTEP1 sends a Type 2 BGP EVPN route (IRB type), which carries the ERT (20:1) of the EVPN instance bound to the BD.
After receiving the BGP Update message, VTEP2 checks the RT value (20:1) carried in the BGP Update message and compares it with the IRT in the local EVPN instance and the IRT (EVPN) in the IP VPN instance. VTEP2 finds that the IRT of the EVPN instance bound to BD 20 and IRT of the IP VPN instance bound to VBDIF 20 are the same, adds the EVPN routes to the EVPN routing table of BD 20, and adds the IP routes contained in the EVPN routes to the routing table of the IP VPN instance bound to VBDIF 20.

## Slide 58: Symmetric IRB: Host IP Route Advertisement (IRB Route)
SW1 (Layer 3 gateway)
VTEP1 1.1.1.1
SW2 (Layer 3 gateway)
VTEP2 2.2.2.2
Router MAC: MAC B
VXLAN tunnel
PC1 172.16.2.1/24
MAC D
PC2 172.16.1.2/24
MAC A
1
SW2 learns the ARP entry of PC2 and generates an IRB route.
2
Destination/Mask | L3VNI | Next Hop | Outbound Interface
172.16.1.2/32 | 1000 | 2.2.2.2 | VXLAN tunnel
SW1 obtains the host route to PC1 and the router MAC address of VTEP1.
IP VPN-Instance VPN1
VXLAN VNI 1000 (L3VNI)
RD 103:1
RT 10:1
---------------------------
BD 10
EVPN VPN-Instance BD_10
RD 10:1
L2 VNI 100
RT 10:1
3
BD 20
VNI 200
BD 10
VNI 100
BGP EVPN uses the EVPN Router's MAC Extended Community attribute to transmit the VTEP's router MAC address, which is the MAC address of an NVE interface.
BGP Update message
Type 2 route
RD 10:1
Host route = 172.16.1.2/32
MAC address = MAC A
L2VNI = 100
L3VNI = 1000
EVPN RT: 10:1
Router MAC: MAC B
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route

## Slide 59: Symmetric IRB: Communication Process
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC D
PC2
172.16.1.2/24
MAC A
BD 20
VNI 200
BD 10
VNI 100
VXLAN tunnel
VTEP2 2.2.2.2
Router MAC: MAC B
IP VPN instance VPN1
BD 20
L3VNI 1000
1
PC1 sends a unicast packet to PC2.
2
VBDIF 20 searches routes in the routing table of the IP VPN instance VPN1. It finds that the next hop of the matched route (32-bit host route) is the remote VTEP of the VXLAN tunnel.
3
VTEP1 sends the data packet to VTEP2 through the VXLAN tunnel.
IP VPN instance VPN1
BD 10
L3VNI 1000
4
VTEP2 searches for the route in the routing table of the IP VPN instance corresponding to VNI 1000 and finds the direct route generated by the local VBDIF interface. VTEP2 then performs Layer 2 table lookup in the corresponding BD.
5
VTEP2 sends the data packet to PC2.
Outer IP
UDP
VXLAN header (L3VNI 1000)
Source MAC address: MAC address of VBDIF 20 Destination MAC address: MAC B
MAC address advertisement
ARP advertisement
IP route advertisement
Type 2 Route
Type 5 Route
Type 3 Route
Notes: In symmetric IRB mode, VTEPs transmit 32-bit host routes generated using ARP entries. Therefore, VTEP1 matches the 32-bit host routes transmitted from VTEP2 during route lookup. Even if VTEP1 has the direct route generated by VBDIF 10, it still forwards packets based on 32-bit host routes according to the longest match rule.
In step 4, VTEP2 decapsulates the VXLAN packet and finds that the destination MAC address of the inner data of a packet is the router MAC address (MAC B) of VTEP2. VTEP2 determines that it needs to forward the packet based on the routing table, finds the corresponding IP VPN instance based on VNI 1000, and searches the routing table of the IP VPN instance for the route, finds the direct route generated by VBDIF 10, searches the local MAC address table, and sends the packet to PC2.

## Slide 60: Type 3 Route
Type 3 route (inclusive multicast route)
  This type of route is used on the VXLAN control plane for automatic VTEP discovery and dynamic VXLAN tunnel establishment.
  VTEPs that function as BGP EVPN peers exchange inclusive multicast routes to transfer L2VNIs and VTEPs' IP addresses.
  The Originating Router's IP Address field identifies the local VTEP's IP address; the MPLS Label field identifies the L2VNI.
Route Distinguisher (8 bytes)
Ethernet Tag ID (4 bytes)
IP Address Length (1 byte)
Originating Router's IP Address (4 or 16 bytes)
RD value of an EVPN instance.
VLAN ID on the device. The value is all 0s in this type of route.
Mask length of the local VTEP's IP address carried in the route.
Local VTEP's IP address carried in the route.
NLRI format
Flags (1 byte)
Tunnel Type (1 byte)
MPLS Label (3 bytes) = L2VNI
Tunnel Identifier (variable)
PMSI attribute
This field is inapplicable in VXLAN scenarios.
The value can only be 6, representing Ingress Replication in VXLAN scenarios.
L2VNI carried in the route.
This field is the local VTEP's IP address in VXLAN scenarios.
Type 2 Route
Type 5 Route
Type 3 Route
Notes: The Provider Multicast Service Interface (PMSI) is an optional transitive BGP attribute. In VXLAN scenarios, Tunnel Type has a fixed value of 6, which is used to carry the VTEP's IP address and L2VNI of the sender.

## Slide 61: VXLAN Tunnel Establishment
VTEPs exchange L2VNIs and VTEP IP addresses through Type 3 routes. If there are reachable routes between the local and remote VTEPs' IP addresses, a VXLAN tunnel is established between the VTEPs. Additionally, if the local and remote VNIs are the same, an ingress replication list is created for BUM packet forwarding.
VTEP 1.1.1.1/32
VTEP 2.2.2.2/32
SW1
SW2
BGP EVPN peer relationship
BGP Update message
Type 3 route
VTEP address = 1.1.1.1
VNI = 1000
BGP Update message
Type 3 route
VTEP address = 2.2.2.2
VNI = 1000
1
2
Dynamic VXLAN tunnel (VNI 1000)
Type 2 Route
Type 5 Route
Type 3 Route

## Slide 62: Type 5 Route
Type 5 route (IP prefix route)
  The IP Prefix Length and IP Prefix fields in an IP prefix route can identify a host IP address or network segment.
  If the IP Prefix Length and IP Prefix fields in an IP prefix route identify a host IP address, the route is used for IP route advertisement in distributed VXLAN gateway scenarios, which functions the same as an IRB route on the VXLAN control plane.
  If the IP Prefix Length and IP Prefix fields in an IP prefix route identify a network segment, the route allows hosts on a VXLAN to access external networks.
Route Distinguisher (8 bytes)
Ethernet Segment Identifier (10 bytes)
Ethernet Tag ID (4 bytes)
IP Prefix Length (1 byte)
IP Prefix (4 or 16 bytes)
GW IP Address (4 or 16 bytes)
MPLS Label (3 bytes)
RD value of an EVPN instance.
Unique ID for defining the connection between local and remote devices.
VLAN ID configured on the device.
Length of the IP prefix carried in the route.
IP prefix carried in the route.
Default gateway address. This field is inapplicable in VXLAN scenarios.
L3VNI carried in the route.
Format of an IP prefix route
Field description
Type 2 Route
Type 5 Route
Type 3 Route

## Slide 63: Application Scenarios of IP Prefix Route Advertisement
For a non-VXLAN network, a VTEP can advertise external routes to the entire VXLAN network through Type 5 routes, instructing hosts on the VXLAN network to access the external network.
VTEP 2.2.2.2/32
Non-VXLAN network
1.2.3.0/24
VNI 88
Static route
1.2.3.0/24
Import the static route to BGP
1
VTEP 1.1.1.1/32
2
3
SW2 obtains the route to 1.2.3.0/24.
SW1 (Layer 3 gateway)
SW2 (Layer 3 gateway)
BGP Update message
Type 5 route
Prefix = 1.2.3.0/24
L3VNI = 88
Type 2 Route
Type 5 Route
Type 3 Route
Notes: Similar to Type 2 IRB routes, Type 5 routes carry the router MAC address of the VTEP through the EVPN router's MAC extended community attribute during route transmission. In addition, Type 5 routes carry only the L3VNI. Therefore, the forwarding process is also called IRB forwarding.

## Slide 64
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
BGP EVPN
  Basic Concepts
  BGP EVPN Routes
  BGP EVPN Features
Campus Network Virtualization

## Slide 65: ARP Broadcast Suppression
BGP EVPN Type 2 routes enable VTEPs to learn MAC addresses without depending on communication between hosts. However, ARP entries between hosts still need to be flooded and forwarded on the VXLAN overlay, which consumes a large number of network resources.
To reduce broadcast traffic, configure ARP broadcast suppression using BGP EVPN routes.
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC A
PC2
172.16.2.2/24
MAC B
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VTEP2
2.2.2.2
1
PC1 sends an ARP Request packet to request the ARP entry of PC2.
3
VTEP1 changes the destination MAC address of the ARP packet from all Fs to MAC B, and sends the ARP packet to VTEP2 through VXLAN encapsulation.
IP Address | MAC | VTEP
172.16.2.2 | MAC B | 2.2.2.2
2
Query the ARP broadcast suppression table of BD 20
Original data packet
VXLAN header
UDP header
IP header
Source IP address: 1.1.1.1
Destination IP address: 2.2.2.2
Source MAC address: MAC A
Destination MAC address: MAC B
ARP
Source MAC: MAC A
Destination MAC: MAC B
4
VTEP2 unicasts the ARP packet to PC2.
Notes: ARP broadcast suppression is an effective method to relieve the burden of a gateway in processing ARP packets. When receiving an ARP Request packet, the gateway searches the ARP broadcast suppression table for the mapping between the IP address and MAC address of the destination device. If the ARP Request packet matches an entry in the table, the gateway replaces the broadcast MAC address in the ARP Request packet with the MAC address of the destination device. Then, the gateway sends the ARP Request packet through the interface corresponding to the destination MAC address.

## Slide 66: Host Information Collection
When ARP broadcast suppression is enabled on a device, the device generates the ARP broadcast suppression table. ARP broadcast suppression entries are originated from Type 2 routes (IRB routes and host ARP advertisement) carried in BGP EVPN packets.
By default, a Layer 3 gateway does not generate BGP EVPN routes based on local ARP information. You need to manually enable BGP EVPN host information collection. The VTEP then generates IRB routes based on ARP entries.
IP Address | MAC
172.16.2.1 | MAC A
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC A
PC2
172.16.2.2/24
MAC B
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VTEP2
2.2.2.2
2
Transmit ARP entries through Type 2 IRB routes
ARP entry of VBDIF 20 (Layer 3 gateway)
3
VTEP2 uses IRB routes to generate an IRB host information table
1
Enable BGP EVPN host information collection to generate IRB routes
Notes: An ARP route carries the following valid information: host MAC address, host IP address, and L2VNI. An IRB route carries the following valid information: host MAC address, host IP address, L2VNI, and L3VNI. As a result, an IRB route includes an ARP route and can be used to advertise both the host IP route and host ARP entry.

## Slide 67: Local Proxy ARP (1)
After BGP EVPN host information collection is enabled on the entire network, the Layer 3 gateway learns the 32-bit host routes of all hosts. In this way, the Layer 3 gateway can use the symmetric IRB mode to forward traffic between hosts in the same BD.
In this case, you can enable local proxy ARP on the VBDIF interface of the Layer 3 gateway. The VBDIF interface responds to the ARP Request packet sent by a downstream host to an IP address on the same network segment. Then the Layer 3 gateway performs Layer 3 forwarding on the same network segment.
VBDIF 20
MAC C
172.16.2.254
arp-proxy local enable
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC A
PC2
172.16.2.2/24
MAC B
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VTEP2
2.2.2.2
1
PC1 sends an ARP Request packet to request the ARP entry of PC2.
2
VBDIF 20 is enabled local proxy ARP to respond to ARP Reply packets.
Notes: On a VXLAN network, a bridge domain (BD) is a Layer 2 broadcast domain. After a VTEP receives BUM packets, it broadcasts the packets in the BD. To reduce broadcast traffic, a network administrator usually configures access-side isolation or port isolation to isolate access users in a BD. However, as services become more diverse and keep increasing, users have growing needs for intra-BD communication. To allow isolated users in a BD to communicate, configure local proxy ARP on the VBDIF interface of the BD.

## Slide 68: Local Proxy ARP (2)
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC A
PC2
172.16.2.2/24
MAC B
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VTEP2
2.2.2.2
4
VTEP1 finds that the destination MAC address is its own MAC address, searches the routing table for the host route, and forwards the packet to VTEP2 through VXLAN.
3
Data packet sent from PC1 to PC2
IP Address | MAC
172.16.2.2 | MAC C
ARP entry of PC1
VBDIF 20
MAC C
172.16.2.254
Payload
Ethernet header
Source MAC address: MAC A
Destination MAC address: MAC C
With the local proxy ARP mechanism, ARP packets are suppressed on the local VTEP, and unnecessary traffic exchange between VTEPs is reduced.

## Slide 69: Distributed Gateway
When local proxy ARP is enabled, a VTEP only needs to maintain local ARP entries. ARP information transmitted by other VTEPs through BGP EVPN routes is not used during forwarding. In this case, the VTEP does not need to maintain ARP entries learned from other VTEPs.
After distributed gateway is enabled, the VTEP processes only the ARP packets received from the user-side host and deletes the learned network-side ARP entries.
VTEP1
1.1.1.1
PC1
172.16.2.1/24
MAC A
PC2
172.16.2.2/24
MAC B
BD 20
VNI 200
BD 20
VNI 200
VXLAN tunnel
VTEP2
2.2.2.2
IP Address | MAC
172.16.2.1 | MAC A
172.16.2.2 | MAC B
VTEP1's ARP entry
Delete
Notes: Generally, the same MAC address is configured for VBDIF interfaces with the same interface number on different VTEPs. After the distributed gateway function is enabled, VBDIF interfaces with the same IP address and MAC address do not report ARP conflicts. In addition, when hosts and VMs are migrated to different VTEPs, the gateway does not need to resolve ARP entries again.

## Slide 70: MAC Mobility (1)
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VTEP3
3.3.3.3
MAC Mobility - Seq 0
Prefix = 172.16.2.1/24
MAC B
Next hop: VTEP1 (1.1.1.1)
172.16.2.1/24
MAC B
VM1
VTEP1 learns the ARP entry of VM1 and generates and advertises an IRB route.
1
3
VM1 is migrated to VTEP2.
VTEP2 detects VM2 based on the ARP entry and generates a new IRB route, which is the same as the route transmitted by VTEP1.
4
For the BGP EVPN route, the sequence number of the extended community attribute MAC Mobility is 0.
2

## Slide 71: MAC Mobility (2)
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VTEP3
3.3.3.3
MAC Mobility - Seq 1
Prefix = 172.16.2.1/24
MAC B
Next hop: VTEP2 (2.2.2.2)
172.16.2.1/24
MAC B
VM1
For the BGP EVPN route, the sequence number of the extended community attribute MAC Mobility is 1.
5
After VTEP1 receives the BGP route update, VTEP1 detects that the VM has been migrated based on the sequence number carried in the MAC Mobility field and sends a BGP Update message to withdraw the previously sent route update.
6
Notes: The MAC Mobility extended attribute is used to announce the location change of a host or VM when the host or VM is migrated from one VTEP to another VTEP.

## Slide 72
Overview of VXLAN and Campus Network Virtualization
Basic Concepts and Fundamentals of VXLAN
BGP EVPN
Campus Network Virtualization

## Slide 73: Layers and Concepts of a VXLAN-based Virtualized Campus Network
Underlay (physical network layer)
Fabric
Border
Edge
Access
Physical network established by physical devices.
Interoperability for all services on the campus network.
Basic bearer network for service data forwarding.
A virtualization technology is used to construct a logical topology based on any physical topology.
A service network is created in the fabric and decoupled from the physical network.
Multiple VNs can be created based on service requirements to implement service isolation.
VXLAN is used to implement Layer 2 and Layer 3 communication.
Edge
Access
Overlay (virtual network layer)
VN 1
VN 2
VN 3
Notes: VXLAN allows a virtual Layer 2 or Layer 3 network (overlay network) to be built over a physical network (underlay network). The overlay network transmits packets between different sites through Layer 3 forwarding paths provided by the underlay network.
In technical applications, different overlay networks are created for different services. Services are aware of the overlay network only. The underlay network is transparent to services.

## Slide 74: Architecture Overview: Network Nodes
Firewall: is required when L4-L7 security policies are deployed. It can be deployed in off-path mode or at the campus egress.
Border node: used to implement communication between the fabric and external networks. It is usually a core switch.
Edge node: a fabric edge device that connects user-side devices to the fabric. Data packets from wired users are encapsulated into VXLAN packets on edge nodes.
Transparent node: a transparent transmission node in the fabric. It does not need to support VXLAN.
Access node: is also known as an extended node. It is an access node for wired users and is optional. It provides network access for users and does not need to support VXLAN.
AP: wireless access node, through which users access the wireless network and finally access the fabric.
Fabric domain (VXLAN)
Access domain
Firewall
Border node
Transparent node
Edge node
Access node
AP
Notes: L4-L7 security policy: The firewall supports security control from Layer 4 to Layer 7.

## Slide 75: What Are an Underlay Network and a Fabric?
Underlay network
Fabric
The underlay network is the foundation of the entire virtualized campus network. It is a physical network consisting of physical network devices, which provides interoperability for all services on a campus network.
Multi-layer architecture (core, aggregation, and access layers)
Multiple topologies (such as tree, ring, and mesh topologies)
Underlay information includes device interconnection VLANs, interconnection IP addresses, and an IGP.
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
IGP (OSPF)
BGP EVPN peer relationship
BGP EVPN peer relationship
A campus fabric is a network resource pool that is abstracted from physical network devices on the underlay network, creating a multiple-purpose network.
The fabric consists of the following resource pools:
Overlay network resource pool (BD IDs and VNIs) for terminal access
VLAN ID pool for terminal access
Access point pool (switch ports for wired access or SSIDs for wireless access) for terminal access
These resource pools can be used to create multiple VNs.
Border
Edge
Edge
Access
Access
Loopback

## Slide 76: What Is an Overlay Network?
Underlay and overlay in our daily life
Urban roads (infrastructure)
A vehicle carrying passengers
Easy access from all directions
Underlay and overlay networks on a virtualized campus network
Underlay network
Overlay network
Service A
Service B
Service A
Service B
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
VXLAN encapsulation
VXLAN encapsulation
Fabric
Notes: An overlay network is a logical network that is constructed based on a physical network using a tunneling technology and with separated forwarding and control planes.

## Slide 77: What Is a VN?
Internet
Border
AP
Host1
Sales employee
Host2
R&D employee
Host3
IoT device
Host4
Guest
OA VN
R&D VN
IoT VN
VXLAN can be used to construct multiple VNs on the underlay network.
A VN is considered as an overlay network.
Service data of each VN is encapsulated using VXLAN in the fabric so that the VN services are isolated on the forwarding plane. The control plane uses BGP EVPN to establish VXLAN tunnels and exchange overlay routing information.
Each VN has the following parameters:
Network service resources (such as the DHCP server and third-party RADIUS/Portal server)
(Optional) External networks
User IP address segments, VLANs, and gateway address
Wired access ports and/or wireless access points (APs)
Other parameters

## Slide 78: Creating a VN
Internet
Border
AP
Host1
Host2
Host3
Host4
OA VN
VN settings
User gateway location
External network
Network service resources
User subnet and gateway
Wired access
Access sites, devices, and ports
Authentication mode
VLAN information
Wireless access
Access sites and devices
1
2
3

## Slide 79: Typical Case Analysis: Requirements
Sales employee
R&D employee
Sales employee
R&D employee
Firewall
Fabric requirements:
Build a fabric based on the physical network.
Use the distributed gateway solution.
VN requirements:
Create two VNs, one for OA and the other for R&D.
By default, the two VNs are completely isolated, and intra-subnet and inter-subnet communication can be implemented in each VN.
Devices in both VNs can access the external network connected to the firewall.
Terminals in the two VNs can obtain IP addresses from the DHCP server.
DHCP server
Internet

## Slide 80: Typical Case Analysis: Fabric Management (1)
Internet
Edge
Edge
Border
Fabric creation and configuration:
You can add physical devices (core, aggregation, and access switches) to the fabric based on service requirements.
You can specify a switch as a border node or an edge node.
iMaster NCE-Campus automatically specifies a border node as an RR to optimize the logical network architecture and BGP peer relationship model.
You can predefine two external networks for two VNs to access the Internet.
You can define a network service resource, which is used by terminals to obtain IP addresses from the DHCP server in the resource.
Firewall
DHCP server
External network 1
Network service resource
External network 2

## Slide 81: Typical Case Analysis: Fabric Management (2)
Automatic deployment of the fabric and underlay network:
Based on the discovered physical network topology and the user-defined fabric, iMaster NCE-Campus automatically orchestrates the network. (You can select multiple OSPF areas or a single OSPF area.)
iMaster NCE-Campus automatically delivers underlay network configurations to devices based on the network orchestration result so that the devices have reachable routes to each other's IP address.
iMaster NCE-Campus automatically delivers fabric configurations to devices, and BGP EVPN peer relationships are established between devices.
Firewall
DHCP server
Edge
Edge
Border
RR
Transparent
Transparent
Interconnection IP address/VLAN
OSPF
Interconnection IP address/VLAN
OSPF
Interconnection IP address/VLAN
OSPF
Interconnection IP address/VLAN
OSPF
BGP EVPN peer relationship

## Slide 82: Typical Case Analysis: VN Management
VN creation:
You can create OA and R&D VNs and specify the IP network segments/VLANs, gateway addresses, associated external networks and network service resources, and terminal access points for the VNs.
iMaster NCE-Campus translates user intents into configurations and delivers the configurations to network devices.
Firewall
DHCP server
OA VN
VLAN 10: 10.1.10.0/24
VLAN 20: 10.1.20.0/24
R&D VN
VLAN 30: 10.1.30.0/24
VLAN 40: 10.1.40.0/24
Access devices and ports
Access devices and ports
External network 1
External network 2
Network service resource

## Slide 83: Typical Case Analysis: Tunnel Establishment
Sales employee
Sales employee
Automatic VXLAN tunnel establishment
BGP EVPN advertises information used to establish VXLAN tunnels between peers.
VXLAN tunnels are established between devices to prepare for subsequent data forwarding.
Firewall
DHCP server
VXLAN tunnel
VXLAN tunnel
VXLAN tunnel

## Slide 84: Typical Case Analysis: Address Obtaining
Sales employee A
Firewall
DHCP server
1.1.1.1
3.3.3.3
1.2.3.0/24
DHCP message exchange
Address obtaining:
After sales employee A accesses the network, the user is authenticated. After the authentication succeeds, the authentication point Edge1 obtains the authorization result of the user and assigns the user to the corresponding VLAN.
Host A sends a DHCP Request message. After receiving the Request message, the gateway Edge1 relays the Request message to the border node through the VXLAN tunnel.
The border node decapsulates the VXLAN packet and forwards the DHCP Request message to the DHCP server.
The DHCP server assigns an IP address to host A.
Edge1
Edge2
Border

## Slide 85: Typical Case Analysis: Intra-Subnet Communication
Sales employee A
10.1.10.1/24
AAAA-0000-0001
Sales employee B
10.1.10.2/24
AAAA-0000-0002
Firewall
DHCP server
1.1.1.1
2.2.2.2
Intra-subnet communication on the same VN:
Sales employees A and B pass the access authentication and access the campus network.
For example, Edge2 advertises the MAC address of host B to the border node through a BGP Update message, and the border node (RR) advertises the MAC address to Edge1.
Edge1 learns the MAC address AAAA.0000.0002.
When host A sends data packets to host B, Edge1 encapsulates the data packets into VXLAN packets and forwards them to Edge2. Edge2 performs VXLAN decapsulation and sends the decapsulated packets to the destination.
VXLAN tunnel (L2VNI)
Route reflection
Edge1
Edge2
Border
BGP Update message
MAC/IP route
MAC address = AAAA-0000-0002
L2VNI = 1000
Next_Hop = 2.2.2.2

## Slide 86: Typical Case Analysis: Inter-Subnet Communication
Sales employee A
10.1.10.1/24
Sales employee C
10.1.20.1/24
Inter-subnet communication on the same VN:
Sales employee C passes the access authentication and accesses the campus network.
Edge2 advertises the host route of host C to the border node through a BGP Update message. The border node (RR) advertises the host route to Edge1.
Edge1 learns the route to 10.1.20.1/32. The next hop of the route is 2.2.2.2, and the outbound interface is the VXLAN tunnel interface.
When host A sends data packets to host C, Edge1 encapsulates the data packets into VXLAN packets and forwards them to Edge2. Edge2 performs VXLAN decapsulation and sends the decapsulated packets to the destination.
Firewall
DHCP server
1.1.1.1
2.2.2.2
VXLAN tunnel (L3VNI)
Route reflection
Edge1
Edge2
Border
BGP Update message
MAC/IP route (IRB)
Host route = 10.1.20.1/32
L3VNI = 10
Next_Hop = 2.2.2.2

## Slide 87: Typical Case Analysis: Accessing the External Network
Sales employee A
10.1.10.1/24
Firewall
DHCP server
1.1.1.1
3.3.3.3
1.2.3.0/24
Accessing the external network:
After you associate the external network (destination network segment 1.2.3.0/24) with the OA VN, iMaster NCE-Campus redistributes the external route to BGP and advertises the route to Edge1 and Edge2.
When host A sends data packets to 1.2.3.0/24, Edge1 encapsulates the data packets into VXLAN packets and sends them to the border node. The border node decapsulates the VXLAN packets and forwards the IP packets to the firewall.
Edge1
Edge2
Border
External route 1.2.3.0/24
Next-hop firewall
BGP route advertisement
Route: 1.2.3.0/24
Next hop: 3.3.3.3
BGP Update message
IP prefix route
Prefix = 1.2.3.0/24
L3VNI = 88
Next_Hop = 3.3.3.3

## Slide 88
(True or false) BGP EVPN Type 2 host IP routes can be used to transmit ARP information. ( )
  True
  False
(Single-answer question) Which of the following statements about BGP EVPN is false? ( )
  MP_REACH_NLRI is used to carry routes.
  The extended community attribute is used to carry routes.
  MP_REACH_NLRI is used to carry L2VNIs and L3VNIs.
  The Next_Hop attribute is used to carry routes.
Notes: A
D

## Slide 89
VXLAN uses a Layer 3 routed network as the underlay network and uses tunnels to build an overlay network, supporting large-scale tenant networks.
VXLAN does not define the control plane. To prevent BUM traffic flooding, use other protocols on the control plane to optimize BUM traffic forwarding.
BGP EVPN defines several new types of BGP EVPN routes by extending BGP. These BGP EVPN routes can be used to transmit VTEP addresses, host information, and routing information, effectively controlling flooding of BUM traffic.