## Slide 1
Datacom
General
V1.0
Zhang Linrui/WX570554
2020.09.01
Zhu Shigeng/00261992
New
Lu Yueyue/WX445705
2020.09.15
Yao Ning/00276205
Update
Lu Yueyue/WX445705
2021.07.15
Wu Yue/WX291773
Update

## Slide 2: Network Admission Control

## Slide 3
Campus networks are faced with an increasing number of information security threats, such as viruses, Trojan horses, spyware, and malicious attacks. On a traditional campus network, the intranet is considered secure and threats come from the extranet. However, research shows that roughly 80% of security threats come from the intranet. Network faults caused by the intranet threats will lead to a broad range of serious damage. Even worse, the service system and network will break down.
The Network Admission Control (NAC) solution integrates terminal security with access control and takes check, isolation, hardening, and audit measures to improve the proactive protection capabilities of terminals. This solution ensures security of each terminal and the entire campus network.

## Slide 4
On completion of this course, you will be able to:
  Describe basic concepts in NAC.
  Learn about typical authentication technologies and their working mechanisms and application scenarios.
  Configure basic user access authentication functions.
  Learn about the functions and working mechanism of policy association.

## Slide 5
Overview of NAC
User Authentication Technologies
User Authorization and Logout
NAC Configuration
Policy Association

## Slide 6: Technical Background of NAC
Unauthorized users may access a campus network, which compromises information security on the campus network.
Various types of terminals are connected to a campus network, and it is difficult to control user behaviors on the campus network.
For security purposes, a campus network cannot grant access rights to all terminals. Authentication must be performed based on user identities and terminal status. The terminals that do not meet certain conditions are not allowed to access the campus network.
Campus network
Unauthorized access
Intranet FTP server
Guest
Virus spreading
Virus spreading
Virus-infected host
Notes: Currently, the intranets of most campus networks are faced with the following security issues:
  Antivirus software is not managed in a centralized manner, and patch management is disordered. Even if enterprises purchase antivirus software, it is difficult to ensure that the virus signature databases of all terminals are the latest. As a result, once a terminal is infected with viruses or malicious code, the virus will soon spread on the intranet.
  User identities cannot be verified. Therefore, unauthorized access cannot be prevented, posing security risks to the network.
  Access control for terminals is not implemented. A user can access all network resources as long as the user successfully connects to the network.

## Slide 7: Overview of NAC
An important design idea of NAC is to allow only authorized users and secure terminals to access networks. NAC provides user authentication, permission management, security check, repair, and upgrade functions to improve the overall terminal security protection capabilities on a campus network.
...
...
User terminals
Admission devices
Admission servers
NAC system architecture
User terminal
  Various terminals such as PCs, mobile phones, printers, and cameras that access the network.
Admission device
  An admission device is an authentication control point that authenticates access users and executes campus security policies to implement access control (for example, allowing or denying user access).
  Admission devices can be switches, routers, APs, VPN gateways, or security devices.
Admission server
  An admission server authenticates and authorizes users. It verifies the user identities of terminals that attempt to access the network, and grants network access rights to authenticated terminals.
  An admission server is typically an authentication server (such as a RADIUS server) or a user data source server that stores user identity information.
Notes: A terminal agent (also known as client software) is usually installed on a user terminal. It works with an admission server to implement user identity authentication, terminal security check, system repair and upgrade, and terminal behavior monitoring and audit.
Admission devices, which can be switches, routers, APs, or other network devices, provide the following functions:
  User identity verification.
  User authentication. Admission devices can implement the commonly used 802.1X authentication, MAC address authentication, and Portal authentication by working with the client software and admission server.
  User permission control.
Admission servers include the security control server, security management server, virus signature database server, and patch server.
  A security control server authenticates users, performs security audit, executes security policies, and works with admission devices to deliver user permissions.
  A security management server manages user information (including adding, deleting, or modifying user permissions and departments), and defines and manages security policies.
  A virus signature database server controls automatic update of the virus signature database in antivirus software on terminals.
  A patch server controls patch installation and update for terminals' operating systems and applications.

## Slide 8: Fundamentals of NAC
User identity authentication request
  An admission device exchanges packets with a terminal to obtain the user credential.
User identity authentication
  The admission device sends the user credential to the admission server for authentication.
User identity verification
  The admission server verifies the identity of the terminal and delivers the verification result and corresponding policy to the admission device.
User policy authorization
  The admission device executes the policy based on the authorization result received from the admission server.
Campus network
Admission server
Admission device
Terminal
User identity authentication request
User identity authentication
User identity verification
User policy authorization
1
2
3
4
Notes: User identity authentication request: A terminal sends the user credential to an admission device.
User identity authentication: The admission device sends the user credential to the admission server for authentication.
User identity verification: The admission server stores user identity information and provides user management functions. After receiving the user credential, the admission server determines whether the terminal identity is valid and delivers the verification result and corresponding policy to the admission device.
User policy authorization: The admission device executes the policy based on the authorization result received from the admission server. For example, the admission device permits or denies access from the terminal. The admission device can also perform more complex policy-based control on the terminal, for example, increasing or decreasing the forwarding priority or limiting the network access rate.

## Slide 9: Policy-based Control in NAC
Campus
network
Policy-based control
  Even if a terminal is authenticated and successfully accesses the network, it does not mean that the terminal can access all resources on the network. Rather, policies are used to grant terminals different network access rights based on user identities.
FTP server
Web server
Email server
Internet
Authenticated guests
Authenticated employees

## Slide 10: Policy-based Authorization in NAC
...
User terminals
...
Admission devices
Access
R&D data
Office data
Marketing data
Post-authentication domain
…
Internet
Intranet
Admission
server
DHCP server
DNS server
…
Pre-authentication domain
Before authentication
After successful authentication
Upon authentication failures
Isolation domain
Virus signature database server
Patch server
…
Notes: The basic NAC process is as follows:
  User can access the network and have the pre-authentication domain network permission before authentication, including access to the access control server, DHCP, and DNS.
  After terminals are successfully authenticated, the admission server delivers network access rights to the admission device to allow users to access resources in the post-authentication domain. For authorized but insecure users, they are granted the rights to access resources in the isolation domain. Only after network vulnerabilities on the terminals are fixed, the admission server grants the rights to access resources in the post-authentication domain to the users. In the isolation domain, users can access resources in the pre-authentication domain to install and upgrade terminal agent software, patches, and antivirus software.
  Unauthorized users and users who have not completed authentication are allowed to access resources only in the pre-authentication domain or isolation domain.

## Slide 11
Overview of NAC
User Authentication Technologies
User Authorization and Logout
NAC Configuration
Policy Association

## Slide 12: Overview of 802.1X Authentication
802.1X client
Access device
Authentication server
Network resources
Introduction
Networking mode
802.1X clients are usually user terminals. A user triggers 802.1X authentication using client software.
An access device is usually a network device that supports 802.1X authentication. It provides a physical or logical interface for clients to access the LAN.
An authentication server, which is typically a RADIUS server, carries out authentication, authorization, and accounting on users.
Application scenario
802.1X authentication applies to office users who have high security requirements.
802.1X authentication is a port-based network access control technology. That is, user identities are verified and network access rights are controlled on ports of access devices.
802.1X authentication uses the Extensible Authentication Protocol over LAN (EAPoL) to exchange authentication information between the client, access device, and authentication server.
802.1X
MAC
Portal
Multi-mode
Notes: The EAP packets transmitted between the client and access device are encapsulated in EAPoL format and transmitted across the LAN.
Users can determine the authentication mode between the access device and authentication server based on the client support and network security requirements.
  EAP termination mode: The access device terminates EAP packets and encapsulates them into RADIUS packets. The authentication server then uses the standard RADIUS protocol to implement authentication, authorization, and accounting.
  EAP relay mode: The access device directly encapsulates the received EAP packets into EAP over RADIUS (EAPoR) packets, and then transmits these packets over a complex network to the authentication server.
EAPoL defines EAP encapsulation on IEEE 802 (such as 802.3 and 802.11) networks. EAPoL only transmits EAP packets between 802.1X clients and access devices, and does not implement authentication.
Typical EAP authentication protocols include Extensible Authentication Protocol Transport Layer Security (EAP-TLS), EAP Tunneled Transport Layer Security (EAP-TTLS), EAP Protected Extensible Authentication Protocol (EAP-PEAP), and EAP Message-Digest Algorithm 5 (EAP-MD5).

## Slide 13: 802.1X Authentication Modes
An access device can process EAPoL packets sent by 802.1X clients in EAP relay or EAP termination mode.
802.1X client
Authentication server
Access device
EAPoL
EAPoR
(EAP over RADIUS)
EAP relay mode
The access device directly encapsulates EAPoL packets sent from the 802.1X client into RADIUS packets without processing data in the EAPoL packets.
This mode has high requirements on the authentication server.
802.1X client
Authentication server
Access device
EAPoL
RADIUS
EAP termination mode
The access device extracts information from EAPoL packets, encapsulates the information into RADIUS packets, and sends the RADIUS packets to the authentication server.
This mode has high requirements on access devices.
802.1X
MAC
Portal
Multi-mode
Notes: EAP relay mode
  This mode simplifies the processing on the access device and supports various authentication methods. However, the authentication server must support EAP and have high processing capability.
  The commonly used authentication modes include EAP-TLS, EAP-TTLS, and EAP-PEAP. EAP-TLS has the highest security because it requires a certificate to be loaded on both the client and authentication server. EAP-TTLS and EAP-PEAP are easier to deploy since the certificate needs to be loaded only on the authentication server, but not the client.
EAP termination mode
  This mode is advantageous in that mainstream RADIUS servers support PAP authentication and CHAP authentication, eliminating the need of server upgrade. However, the workload on the access device is heavy because it needs to extract the client authentication information from the EAP packets sent by the client and encapsulate the information using the standard RADIUS protocol. In addition, the access device does not support other EAP authentication methods except MD5-Challenge.
  The major difference between PAP and CHAP is that passwords in CHAP authentication are transmitted in cipher text, whereas passwords in PAP authentication are transmitted in plain text. In this aspect, CHAP provides higher security and is recommended.

## Slide 14: 802.1X Authentication Process
EAP-MD5 authentication in EAP relay mode is used as an example.
User terminal
Access device
Authentication server
1. EAPoL-Start
The user initiates authentication.
2. EAP-Request/identity
What's your user name?
3. EAP-Response/identity
My user name is Hello.
4. RADIUS Access-request
5. RADIUS Access-challenge
Generate a random number.
6. EAP Request/MD5 challenge
7. EAP-Response/MD5 challenge response
Cipher text calculated using the password and random number
8. RADIUS Access-request
9. RADIUS accept
10. EAP-Success
Port in authorized state
  Triggered by a client: When a user starts the client and enters the user name and password, the client sends an EAP packet to the access device to trigger authentication.
  Triggered by an access device: When receiving a DHCP or ARP packet from a user terminal, the access device proactively enables the user terminal to display the client page and prompt the user to enter the user name and password. After the user name and password are entered, authentication is started.
Authentication triggering modes
  Port-based access control: allows subsequent users on a port to access the network once a user has been authenticated on the port. When the first user goes offline, all the other users cannot use network resources.
  MAC address–based access control: requires each user on a port to be authenticated separately before granting them access to the network. When a user goes offline, other users are not affected.
802.1X access control
802.1X
MAC
Portal
Multi-mode
Notes: EAP relay authentication process:
  When a user needs to access an external network, the user starts the 802.1X client, enters the applied and registered user name and password, and initiates a connection request. The client then sends an authentication request packet (EAPoL-Start) to the access device to start the authentication process.
  After receiving the authentication request packet, the access device returns an EAP-Request/Identity packet, requesting the client to send the previously entered user name.
  In response to the request sent by the access device, the client sends an EAP-Response/Identity packet containing the user name to the access device.
  The access device encapsulates the EAP-Response/Identity packet into a RADIUS Access-Request packet and sends the RADIUS packet to the authentication server.
  After receiving the user name forwarded by the access device, the RADIUS server searches the user name table in the local database for the corresponding password, encrypts the password with a randomly generated MD5 challenge, and sends a RADIUS Access-Challenge packet containing the MD5 challenge to the access device.

## Slide 15
Notes:   The access device forwards the MD5 challenge received from the RADIUS server to the client.
  Upon receipt of the MD5 challenge, the client encrypts the password with the MD5 challenge, generates an EAP-Response/MD5-Challenge packet, and sends the packet to the access device.
  The access device encapsulates the EAP-Response/MD5-Challenge packet into a RADIUS Access-Request packet and sends the RADIUS packet to the RADIUS server.
  The RADIUS server compares the received encrypted password with the locally encrypted password. If the two passwords match, the user is considered valid and the RADIUS server sends a packet indicating successful authentication (RADIUS Access-Accept) to the access device.
  After receiving the RADIUS Access-Accept packet, the access device sends a packet indicating successful authentication (EAP-Success) to the client, changes the port state to authorized, and allows the user to access the network through the port.
In EAP termination mode, the MD5 challenge for encrypting the user password is randomly generated by the access device, instead of the authentication server in EAP relay mode. Besides, in EAP termination mode, the access device encapsulates the user name, password encrypted by the client, and MD5 challenge into standard RADIUS packets, and sends the packets to the authentication server for authentication. In EAP relay mode, in contrast, the access device is only responsible for encapsulating EAP packets into RADIUS packets and transparently transmitting them to the authentication server.

## Slide 16: Basic 802.1X Authentication Configuration (1)
[Huawei] dot1x-access-profile name access-profile-name
Create an 802.1X access profile and enter the 802.1X access profile view.
The device uses 802.1X access profiles to uniformly manage all 802.1X access configurations. By default, the device has a built-in 802.1X access profile named dot1x_access_profile.
[Huawei-dot1x-access-profile-ProfileName] dot1x authentication-method { chap | pap | eap }
Configure an authentication mode for 802.1X users.
In 802.1X authentication, the device supports two authentication modes:
EAP termination: The device parses EAP packets, encapsulates user authentication information into RADIUS packets, and sends the packets to the RADIUS server for authentication. You can specify the chap or pap parameter to configure the authentication mode between the device and RADIUS server.
EAP relay: The device directly encapsulates the received EAP packets containing user authentication information into RADIUS packets, and sends the RADIUS packets to the RADIUS server. This mechanism is also known as EAP over RADIUS (EAPoR).
802.1X
MAC
Portal
Multi-mode

## Slide 17: Basic 802.1X Authentication Configuration (2)
[Huawei-dot1x-access-profile-ProfileName] authentication trigger-condition { dhcp | arp | dhcpv6 | nd | any-l2-packet }
Configure the type of packets that can trigger 802.1X authentication.
After 802.1X authentication is enabled, DHCP, DHCPv6, ND, and ARP packets can trigger 802.1X authentication by default.
[Huawei-GigabitEthernet0/0/1] l2protocol-tunnel user-defined-protocol protocol-name enable
Configure Layer 2 transparent transmission of 802.1X authentication packets.
In the 802.1X authentication scenario, if there is a Layer 2 switch between the 802.1X-enabled access device and users, Layer 2 transparent transmission of 802.1X authentication packets must be enabled on the Layer 2 switch; otherwise, users cannot be successfully authenticated.
The l2protocol-tunnel user-defined-protocol command defines Layer 2 protocol packets, including the protocol name, multicast destination MAC address (specified by protocol-mac), and replacement multicast MAC address (group-mac). For 802.1X authentication, values of the protocol-mac and group-mac parameters are 0180-c200-0003 and 0100-0000-0002, respectively.
The l2protocol-tunnel enable command enables Layer 2 protocol tunneling on an interface.
[Huawei] l2protocol-tunnel user-defined-protocol protocol-name protocol-mac protocol-mac group-mac group-mac
802.1X
MAC
Portal
Multi-mode

## Slide 18: Summary of 802.1X Authentication
802.1X authentication is a port-based network access control technology that encapsulates protocol packets in EAPoL format.
You can set 802.1X authentication parameters based on the actual network requirements or device capabilities:
  802.1X access control: interface-based or MAC address–based
  Authentication mode: EAP termination or EAP relay
  Authentication triggering mode: triggered by a client or access device
  Authentication protocol: EAP-TLS, EAP-TTLS, EAP-PEAP, or EAP-MD5
802.1X
MAC
Portal
Multi-mode

## Slide 19: Overview of MAC Address Authentication
802.1X
MAC
Portal
Multi-mode
MAC address authentication process
  User terminals do not require any client software.
  MAC address authentication applies to dumb terminals such as IP phones and printers.
Application scenario
1. ARP, DHCP, ND, or DHCPv6 packet, triggering MAC address authentication
2. RADIUS authentication request packet containing the user name and password
3. Authentication success
Dumb terminal
Port in authorized state
Access device
Authentication server
  The authentication client, access device, and authentication server are deployed.
Networking mode
  MAC address authentication controls network access rights of users based on interfaces and user MAC addresses.
  User terminals are authenticated by the authentication server based on their MAC addresses.
  By default, the switch triggers MAC address authentication on users after receiving DHCP, ARP, DHCPv6, or ND packets. You can also configure the switch to trigger MAC address authentication after receiving any data frame.
Introduction
Notes: Dumb terminal: Compared with other terminals, dumb terminals have limited functions and simple interaction modes. In this document, dumb terminals refer to terminals whose authentication information such as user names and passwords cannot be entered.
By default, a MAC address without hyphens (-) is used as the user name and password for MAC address authentication, for example, 0005e0112233.
Passwords of MAC address authentication users can be processed using PAP or CHAP. The following MAC address authentication process uses PAP as an example:
  When a terminal accesses the network, the access device detects and learns the MAC address of the terminal, triggering MAC address authentication.
  The access device generates a random value (MD5 challenge), arranges the user MAC address, password, and random value in sequence, encrypts them using the MD5 algorithm, encapsulates the encryption results into a RADIUS authentication request packet, and sends the packet to the RADIUS server.
  The RADIUS server arranges the user MAC address, password saved in the local database, and received random value in sequence, and uses the random value to encrypt them using the MD5 algorithm. If the encrypted password is the same as that received from the access device, the RADIUS server sends an authentication accept packet to the access device, indicating that MAC address authentication is successful and the terminal is allowed to access the network.
Different from PAP, CHAP arranges CHAP ID，the user MAC address, and random value in sequence, encrypts them using the MD5 algorithm.

## Slide 20: MAC Address Authentication Configuration (1)
[Huawei] mac-access-profile name access-profile-name
Create a MAC access profile and enter the MAC access profile view.
The device uses MAC access profiles to uniformly manage access configurations of MAC address authentication users. By default, the device has a built-in MAC access profile named mac_access_profile.
[Huawei-mac-access-profile-ProfileName] mac-authen authentication-method { chap | pap }
Configure an authentication mode for MAC address authentication users.
By default, PAP authentication is used.
During MAC address authentication, the access device and authentication server exchange RADIUS packets in either PAP or CHAP mode. CHAP is more secure than PAP.
[Huawei-mac-access-profile-ProfileName] authentication trigger-condition { dhcp | arp | dhcpv6 | nd | any-l2-packet }
Configure the type of packets that can trigger MAC address authentication.
By default, DHCP, ARP, DHCPv6, and ND packets can trigger MAC address authentication.
802.1X
MAC
Portal
Multi-mode

## Slide 21: MAC Address Authentication Configuration (2)
[Huawei-mac-access-profile-ProfileName] mac-authen username { fixed username [ password cipher password ] | macaddress [ format { with-hyphen | without-hyphen } [ password cipher password ] ]}
Configure the user name format for MAC address authentication.
fixed username specifies a fixed user name for MAC address authentication. If no password is configured, users can log in without a password, which is not recommended.
macaddress specifies the MAC addresses of users as user names for MAC address authentication. If no password is configured, the MAC address of a user is used as the password. When local authentication is used, a password must be configured.
  with-hyphen: indicates that the MAC address contains delimiters.
  without-hyphen: indicates that the MAC address does not contain delimiters.
802.1X
MAC
Portal
Multi-mode

## Slide 22: Overview of Portal Authentication
Client
Portal server
Access device
Authentication server
Introduction
Application scenario
Portal authentication does not require dedicated client software. Therefore, it is primarily used in access scenarios without client software or guest access scenarios.
Portal authentication is also known as web authentication. Users enter their user names and passwords on the web authentication page for identity authentication.
Users can access the authentication page in either of the following ways:
  Proactive authentication: Users proactively access the Portal authentication website through browsers.
  Redirect authentication: When the access address entered by a user is not the address of the Portal authentication website, the access device forcibly redirects the user to the Portal authentication website.
Networking mode
The authentication client, access device, Portal server, and authentication server are deployed.
802.1X
MAC
Portal
Multi-mode
Notes: Client: In most cases, a client is a host where an HTTP/HTTPS-capable browser is installed.
Access device: a network device such as a switch or router, which provides the following functions:
  Redirects all HTTP and HTTPS requests of users on authentication subnets to the Portal server before authentication is performed.
  Interacts with the Portal server and authentication server to implement user authentication, authorization, and accounting.
  Grants users access to specified network resources upon successful authentication.
Portal server: a server system that receives authentication requests from clients, provides Portal services and authentication pages, and exchanges client authentication information with access devices.
Authentication server: interacts with access devices to implement user authentication, authorization, and accounting.

## Slide 23
Notes: Portal authentication has the following advantages:
  Ease of use: In most cases, Portal authentication authenticates a user on a web page, without any additional software required on the client.
  Convenient operations: Portal authentication allows for value-added services on the web page, including advertisement push and enterprise publicity.
  Mature technology: Portal authentication has been widely used on networks of carriers, fast food chains, hotels, and schools.
  Flexible deployment: Portal authentication implements access control at the access layer or at the ingress of key data.
  Flexible user management: Portal authentication can be performed on users based on the combination of user names and any one of VLANs, IP addresses, and MAC addresses.

## Slide 24: Overview of the Portal Authentication Process
Client
Portal server
Access device
Authentication server
1. Establish a pre-connection (required only for Layer 2 networking).
2. Send an HTTP connection request.
3. Redirect the HTTP request to the Portal server.
4. Send an HTTP connection request.
5. Return the Portal page.
6. Send a Portal authentication request.
Portal-based Portal authentication
HTTP/HTTPS-based Portal authentication
7. Perform authentication using either protocol.
When the client and access device are connected through a Layer 2 network, configure Layer 2 Portal authentication.
When the client and access device are connected through a Layer 3 network, configure Layer 3 Portal authentication.
The Portal protocol is used between the Portal server and access device.
The HTTP/HTTPS protocol is used between the client and access device.
Portal authentication modes
Portal authentication protocols
The HTTP/HTTPS protocol is used between the client and Portal server.
Portal access protocols
802.1X
MAC
Portal
Multi-mode
Notes: Select a Portal authentication mode based on the actual network requirements.
  When Layer 2 authentication is used, the device can learn users' MAC addresses and identify the users based on their MAC addresses and IP addresses. Layer 2 authentication provides a simple authentication process while ensuring high security. However, users must be in the same network segment as the access device, causing inflexible networking.
  When Layer 3 authentication is used, the device cannot obtain the MAC address of a client, so it identifies the user based only on the client IP address. Layer 3 authentication allows for flexible networking and facilitates remote control. However, users can only be identified based on their IP addresses, leading to poor security.
The Portal authentication process is as follows:
  Before authentication, the client establishes a pre-connection with the access device. The access device creates a user online entry for the client and grants the client access to certain network resources. The Layer 3 authentication process is similar to the Layer 2 authentication process, except that no pre-connection is established between the client and access device.
  The client initiates an HTTP connection request.

## Slide 25
Notes:   Upon receipt of the HTTP connection request packet, the access device determines whether to permit the packet. If the HTTP packet is destined for the Portal server or a publicly available network resource, the access device permits the packet. If the HTTP packet is destined for other addresses, the access device sends the uniform resource locator (URL) of the Portal authentication page to the client.
  The client sends an HTTP connection request to the Portal server based on the obtained URL.
  The Portal server returns the Portal authentication page to the client.
  The user enters the user name and password on the Portal authentication page. The client then sends a Portal authentication request to the Portal server.
  The parameters such as the user name and password are transmitted according to the protocol interaction process defined by different authentication protocols.

## Slide 26: Portal Authentication Process: Using the Portal Protocol
7. Send a Portal challenge request.
8. Return a Portal challenge response.
9. Send a Portal authentication request.
10. Exchange RADIUS authentication and accounting information.
11. Send the Portal authentication result.
12. Notify the user of the authentication result.
13. Acknowledge the authentication result.
Client
Portal server
Access device
Authentication server
6. Send a Portal authentication request.
The Portal protocol is used between the Portal server and access device for transmitting parameters such as the user name and password. Generally, the Portal protocol is recommended.
This protocol has the following features:
Adopts the client/server model and runs based on UDP.
Supports CHAP authentication (more secure) and PAP authentication.
Uses packets with attribute information such as the user name, password, and MAC address encapsulated in TLV format.
Authentication protocol: Portal
Portal-based Portal authentication
802.1X
MAC
Portal
Multi-mode
Notes: The following uses CHAP authentication as an example to describe the Portal-based Portal authentication process:
  After receiving the Portal authentication request, the Portal server sends a Portal challenge request packet to the access device. This step is performed only when CHAP authentication is used between the Portal server and access device. If PAP authentication is used, steps 7 and 8 are not performed.
  The access device sends a Portal challenge response packet to the Portal server.
  The Portal server encapsulates the entered user name and password into a Portal authentication request packet and sends the packet to the access device.
  The access device and RADIUS server exchange user information to authenticate the user, including:
    The access device encapsulates the entered user name and password into a RADIUS authentication request packet and sends the packet to the RADIUS server.

## Slide 27
Notes:     The RADIUS server authenticates the user name and password. If authentication succeeds, the RADIUS server sends an authentication accept packet to the access device. If authentication fails, the RADIUS server sends an authentication reject packet to the access device. The authentication accept packet also contains user authorization information because RADIUS authorization is combined with authentication.
    The access device permits or denies the user access according to the authentication result. If the user access is permitted, the access device sends an accounting start request packet to the RADIUS server.
    The RADIUS server replies with an accounting start response packet, starts accounting, and adds the user to the local online user list.
  The access device sends the Portal authentication result to the Portal server and adds the user to the local online user list.
  The Portal server sends the Portal authentication result to the client to inform the client of successful authentication and adds the user to the local online user list.
  The Portal server sends an authentication acknowledgment packet to the access device.
Note: If the built-in Portal server function of an access device is used for Portal authentication, only the Portal protocol is supported.

## Slide 28: Portal Authentication Process: Using the HTTP/HTTPS Protocol
HTTP/HTTPS-based Portal authentication
8. Send an authentication request (HTTP/HTTPS).
https://Portal.example.com/login?userName=test&password=Huawei@123
9. Exchange RADIUS authentication and accounting information.
10. Return the Portal authentication result.
Client
Portal server
Access device
Authentication server
6. Send a Portal authentication request.
7. Instruct the client to send an authentication request to the access device.
The HTTP/HTTPS protocol is used between a client and an access device for transmitting parameters such as the user name and password. If the Portal server does not support the Portal protocol, use HTTP/HTTPS as the authentication protocol.
The client directly sends user information to the access device in HTTP request mode. Currently, the POST and GET request methods are supported.
  POST (supported by default): The requested data is stored in the body of an HTTP request packet and is not a part of a URL.
  GET: The requested data is appended to a URL and separated from the URL by a question mark (?). The data is a part of the URL, so it is visible to all users.
Authentication protocol: HTTP/HTTPS
802.1X
MAC
Portal
Multi-mode
Notes: HTTPS is a secure HTTP and also known as HyperText Transfer Protocol over Transport Layer Security (HTTP over TLS) or HyperText Transfer Protocol over Secure Socket Layer (HTTP over SSL). HTTPS uses HTTP for communication and SSL/TLS for data encryption.
A URL is a concise representation of the location and access method of a resource that can be obtained from the Internet. It is the address of a standard resource on the Internet. Each file on the Internet has a unique URL. The URL contains information about the location of the file and how a browser should process the file.
When HTTP/HTTPS-based Portal authentication is used, the authentication process is as follows:
  The Portal server instructs the client to send a Portal authentication request to the access device.
  The client sends a Portal authentication request to the access device.
  After receiving the Portal authentication request, the access device parses the packet according to parameter names to obtain parameters such as the user name and password, and then sends the obtained user name and password to the RADIUS server for authentication. The process is similar to the Portal-based Portal authentication.
  The access device returns the Portal authentication result to the client and adds the user to the local online user list.
As shown in the figure, an HTTP request is sent in Get mode: https://Portal.example.com/login?userName=test&password=Huawei@123. You can see that the user name and password are in plain text and are separated from the URL by a question mark (?).

## Slide 29: Portal Authentication Configuration - Configuring an External Portal Server (1)
[Huawei] portal web-authen-server { http | https ssl-policy policy-name } [ port port-number ]
Enables Portal interconnection using the HTTP/HTTPS protocol.
When HTTP/HTTPS-based Portal authentication is used, you need to enable Portal interconnection using the HTTP/HTTPS protocol on the device. If HTTPS is used, you also need to specify an SSL policy name.
[Huawei] web-auth-server server-name
Create a Portal server template and enter the Portal server template view.
A Portal server template is used to uniformly configure parameters of an external Portal server, such as the IP address and URL of the Portal server.
[Huawei-web-auth-server-ServerName] protocol { http [ password-encrypt { none | uam } ] | portal }
Configure the protocol used for Portal authentication.
You can configure the HTTP/HTTPS or Portal protocol for Portal authentication based on your network requirements.
802.1X
MAC
Portal
Multi-mode

## Slide 30: Portal Authentication Configuration - Configuring an External Portal Server (2)
[Huawei-web-auth-server-ServerName] server-ip server-ip-address &<1-10>
Configure parameters for the Portal server when the Portal protocol is used for Portal authentication.
Command functions:
server-ip: configures the IP address of the Portal server.
source-ip: configures the IP address used by the device to communicate with the Portal server.
shared-key: configures the shared key used by the device to exchange information with the Portal server.
url: configures a redirect URL or pushed URL to be sent to access terminals.
[Huawei-web-auth-server-ServerName] source-ip ip-address
[Huawei-web-auth-server-ServerName] shared-key cipher key-string
[Huawei-web-auth-server-ServerName] url url-string
[Huawei-web-auth-server-ServerName] url url-string
Configure parameters for the Portal server when the HTTP/HTTPS protocol is used for authentication.
Only the URL of the Portal server needs to be configured.
802.1X
MAC
Portal
Multi-mode

## Slide 31: Portal Authentication Configuration - Configuring a Portal Access Profile
[Huawei] portal-access-profile name access-profile-name
Create a Portal access profile and enter the Portal access profile view.
The device uses Portal access profiles to uniformly manage all access configurations of Portal users.
By default, the device has a built-in Portal access profile named portal_access_profile.
[Huawei-portal-acces-profile-ProfileName] web-auth-server server-name { direct | layer3 }
Configure a Portal server template used by the Portal access profile.
When a user in the Portal access profile accesses restricted network resources, the HTTP request of the user is forcibly redirected to the authentication page of the Portal server for Portal authentication.
If there is no Layer 3 forwarding device between the user and device (authentication point), specify the direct parameter to enable Layer 2 Portal authentication. In this mode, the device identifies users based on their IP addresses and MAC addresses.
When a Layer 3 forwarding device exists between the user and device, specify the layer3 parameter to enable Layer 3 Portal authentication. In this mode, the device identifies users based only on their IP addresses.
802.1X
MAC
Portal
Multi-mode

## Slide 32: Comparison Between User Authentication Technologies
Huawei NAC solution supports various user authentication technologies, including 802.1X authentication, MAC address authentication, and Portal authentication. Authentication points can be flexibly deployed on network devices such as access switches, aggregation switches, access controllers (ACs), routers, and firewalls to implement NAC by working with iMaster NCE-Campus.
Item | 802.1X Authentication | Portal Authentication | MAC Address Authentication
Client software | Required | Not required | Not required
Advantage | High security | Flexible deployment | Client software not required
Disadvantage | Inflexible deployment | Low security | MAC address registration required, making management complicated
Application scenario | New network with concentrated users and high requirements for security | Scenario with scattered and moving users | Access authentication of dumb terminals such as printers and fax machines
802.1X
MAC
Portal
Multi-mode

## Slide 33: MAC Address Bypass Authentication
802.1X authentication, MAC address authentication, and Portal authentication have their own characteristics. You can use multi-mode authentication to meet authentication requirements in different scenarios.
Access device
Authentication server
Terminals
1. Send traffic.
3. Perform 802.1X authentication.
4. Perform MAC address authentication.
802.1X authentication times out, and MAC address authentication is performed.
2. Trigger 802.1X authentication.
Dumb terminals such as printers and fax machines do not support 802.1X authentication. When both PCs and dumb terminals are connected to an interface of an access device, you can configure MAC address bypass authentication to allow the dumb terminals to access the network using MAC address authentication.
MAC address bypass authentication takes a longer period of time than MAC address authentication because it has an 802.1X authentication stage additionally.
802.1X
MAC
Portal
Multi-mode

## Slide 34: MAC Address-Prioritized Portal Authentication
Access device
Portal server
Terminal
RADIUS server
1. Send HTTP traffic when a user browses a web page.
2. Perform MAC address authentication, which fails.
3. Redirect the user's HTTP request to the Portal authentication page.
4. Perform Portal authentication, which succeeds.
5. The user logs out.
6. The user continues to access the network within the validity period of the MAC address.
7. Perform MAC address authentication, which succeeds because the user's MAC address has been cached on the RADIUS server.
8. The user accesses the network without the need of re-authentication.
If a user who has passed Portal authentication disconnects from the network, the user needs to enter the user name and password again to reconnect to the network. This results in low user experience.
Background
MAC address-prioritized Portal authentication is introduced to resolve this problem. With this function, users no longer need to enter their user names and passwords again to reconnect to the network within the validity period of terminal MAC addresses.
To use this function, configure MAC address authentication and Portal authentication on the access device, and enable MAC address-prioritized Portal authentication and set the MAC address validity period on the authentication server.
MAC address-prioritized Portal authentication
802.1X
MAC
Portal
Multi-mode
Notes: After passing Portal authentication, terminals may be disconnected from the wireless network when they move from one wireless signal coverage area to another or when the wireless signal is unstable. In this case, users need to enter their user names and passwords for identity authentication every time the terminals go online, leading to poor network access experience. MAC address-prioritized Portal authentication is used to resolve this problem. Generally, there is no need to enable MAC address-prioritized Portal authentication on wired networks that provide stable signals.

## Slide 35
Overview of NAC
User Authentication Technologies
User Authorization and Logout
NAC Configuration
Policy Association

## Slide 36: Authorization After Successful Authentication
Authentication checks whether the identity of a user who attempts to access the network is valid. Authorization specifies the network access rights that the authorized user can have, that is, the accessible resources.
Using RADIUS server authorization as an example, the typical authorization information includes:
  VLAN: To prevent unauthenticated users from accessing restricted network resources, the restricted network resources and unauthenticated users are divided into different VLANs. After a user is authenticated, the RADIUS server delivers an authorized VLAN to the user.
  ACL: After a user is authenticated, the RADIUS server assigns an authorized ACL to the user. Then, the access device controls the user packets according to the ACL.
  UCL group: A User Control List (UCL) group is a collection of network terminals such as PCs and smartphones. The administrator can add users who have the same network access requirements to one UCL group, and configure network access policies for the UCL group. Compared with the solution in which access control policies are deployed for each user, the UCL group–based access control solution greatly reduces the administrator's workload.
User Authorization
User Logout
Notes: When the RADIUS server is used, the authentication accept packet also contains user authorization information because RADIUS authorization is combined with authentication.
VLAN-based authorization by the RADIUS server:
  After a user is authenticated, the RADIUS server delivers an authorized VLAN to the user. The access device then changes the VLAN to which the user belongs to the authorized VLAN, with the interface configuration remaining unchanged. The authorized VLAN has a higher priority than the VLAN configured on the interface. That is, the authorized VLAN takes effect after the authentication succeeds, and the configured VLAN takes effect when the user is offline.
The RADIUS server can assign an authorized ACL to a user in either of the following modes:
  Static ACL assignment: The RADIUS server uses the standard RADIUS attribute Filter-Id to assign an ACL ID to the user. In this mode, the ACL and corresponding rules are configured on the access device in advance.
  Dynamic ACL assignment: The RADIUS server uses the Huawei extended RADIUS attribute HW-Data-Filter to assign an ACL ID and corresponding rules to the user. In this mode, the ACL ID and ACL rules are configured on the RADIUS server.

## Slide 37
Notes: The RADIUS server assigns an authorized UCL group to a user in either of the following modes:
  Assigns the UCL group name through the standard RADIUS attribute Filter-Id.
  Assigns the UCL group ID through the Huawei extended RADIUS attribute HW-UCL-Group.
  You must configure the UCL group and corresponding network access policies on the access device in advance, regardless of which UCL group authorization mode is used.
RADIUS is a fully extensible protocol. The No. 26 attribute (Vendor-Specific) defined in RFC 2865 can be used to extend RADIUS to implement the functions not supported by standard RADIUS attributes. For details about Huawei extended RADIUS attributes, see the product documentation.
For more information, see the Free Mobility course.

## Slide 38: Authentication-Free and Authentication Event Authorization
Before being authenticated, users need to obtain some network access rights to meet basic network access requirements such as downloading the 802.1X client and updating the virus signature database.
Authentication-free (free-rule)
Authorization parameters
Service scheme: Parameters such as the UCL group, VLAN, and QoS profile can be bound to a service scheme.
VLAN: Users are granted the permission to access resources in a specified VLAN.
Users are allowed to access 192.168.1.1 to download client software before being authenticated
Terminal
Access device
Software server
192.168.1.1
Able to access 192.168.1.1 without authentication
Authentication event authorization
Users require certain rights when encountering different events (such as pre-authentication, authentication failure, and authentication server failure) during authentication.
Authentication-free rule profile
(free-rule-template)
Method 1: common authentication-free rule, which is determined by parameters such as the IP address, MAC address, source interface, and VLAN.
Method 2: Associate an ACL.
User group (UCL group): Network access rights are assigned to a user group with members having the same network access requirements.
Users are allowed to access 192.168.1.1 to update the virus signature database even when authentication fails.
Terminal
Access device
Virus signature database server
192.168.1.1
Able to access 192.168.1.1 when authentication fails
User Authorization
User Logout
Notes: When an authentication-free rule is configured using an ACL, the ACL number is in the range from 6000 to 6031.
The NAC escape mechanism grants specified network access rights to users when the authentication server is Down or to users who fail the authentication or are in pre-connection state. The escape solutions vary according to the authentication modes. Some escape solutions are shared by all authentication modes, while some are supported only in specific authentication modes. For details, see "NAC Escape Mechanism" in the product documentation.

## Slide 39: User Logout
When users go offline but the access device, RADIUS server, and Portal server do not detect the user logout events, the following problems may occur:
  The RADIUS server still performs accounting for the users, causing incorrect accounting.
  Unauthorized users may spoof IP addresses and MAC addresses of authorized users to access the network.
  If there are many offline users, these users are still counted as access users of the device. As a result, other users may fail to access the network.
The access device needs to detect user logout immediately, delete the user entry, and request the RADIUS server to stop accounting.
User logout may occur in the following situations:
  A client logs out proactively.
  An access device controls user logout.
  The server forces a user to go offline.
User Authorization
User Logout
Notes: Note:
  MAC address authentication supports only user logout control by the access device and server.
  Portal authentication allows both the authentication server and Portal server to control user logout.

## Slide 40
Overview of NAC
User Authentication Technologies
User Authorization and Logout
NAC Configuration
Policy Association

## Slide 41: User Access Authentication Configuration Roadmap
Bind the access profile to an authentication profile.
Interface or VAP profile
Authentication profile
...
Configure an access profile.
802.1X access profile (dot1x-access-profile)
MAC access profile (mac-access-profile)
Portal access profile (portal-access-profile)
1
Configure an authentication profile.
Authentication mode (including the access profile)
User authorization
…
2
Apply the authentication profile to enable NAC.
3
Configure AAA.
AAA schemes
Authentication scheme
Authorization scheme
Accounting scheme
Configure a RADIUS server template or a local user.
Bound to
Domain
Authenticate users in the corresponding domain.
Extended functions
Notes: VAP indicates a virtual access point.
VAP profile: Configure WLAN parameters in a VAP profile, and bind the VAP profile to an AP group or AP. Then, a VAP is generated on the AP to provide wireless access services for STAs.

## Slide 42: Authentication Profile Configuration (1)
[Huawei] authentication-profile name authentication-profile-name
Create an authentication profile and enter the authentication profile view.
You can configure parameters in an authentication profile to implement varying access control for different users on the device. After configuring an authentication profile, apply it to an interface or a VAP profile to enable NAC.
[Huawei-authen-profile-ProfileName] dot1x-access-profile access-profile-name
Bind an access profile to an authentication profile.
[Huawei-authen-profile-ProfileName] mac-access-profile access-profile-name
[Huawei-authen-profile-ProfileName] portal-access-profile access-profile-name
You can bind an access profile of the required type to an authentication profile. When more than one access profile is bound to an authentication profile, multi-mode authentication is used. There is no limitation on the sequence of binding access profiles. The device triggers authentication of a specific type based on the authentication packet received. You can bind one 802.1X access profile, one MAC access profile, and one Portal access profile to the same authentication profile at most.

## Slide 43: Authentication Profile Configuration (2)
[Huawei-authen-profile-ProfileName] authentication dot1x-mac-bypass
Enable MAC address bypass authentication.
MAC address bypass authentication combines 802.1X authentication and MAC address authentication. Before enabling this function in an authentication profile, ensure that an 802.1X access profile and a MAC access profile have been bound to the authentication profile.
[Huawei-authen-profile-ProfileName] access-domain domain-name [ dot1x | mac-authen | portal ] * [ force ]
Configure a default domain or forcible domain for users.
The device manages users in domains. force configures a forcible domain. If this parameter is not specified, a default domain is configured. The dot1x, mac-authen, and portal parameters specify the type of users for whom a default domain or forcible domain is configured.
When a default domain is configured, the device authenticates users based on the domain names contained in the user names. If a user name does not contain any domain name, the device authenticates the user in the default domain.
When a forcible domain is configured, the device authenticates users in the forcible domain, regardless of whether the user names contain domain names.

## Slide 44: Extended Function: Configuring Static Users
During network deployment, static IP addresses are assigned to dumb terminals such as printers, which can be configured as static users for flexible authentication.
[Huawei] static-user start-ip-address [ end-ip-address ] [ domain-name domain-name | interface interface-type interface-number | mac-address mac-address | vlan vlan-id ] *
Configure parameters such as the IP address range, domain name, connected interface, and VLAN for a static user.
[Huawei] static-user username macaddress format { with-hyphen [ normal ] [ colon ] | without-hyphen } [ uppercase ] [ password-with-macaddress ]
Configure parameters such as the user name and password of the static user.
[Huawei] static-user username format-include { ip-address | mac-address | system-name }
[Huawei] static-user password cipher password
After a static user is configured, you can enable 802.1X authentication, MAC address authentication, or Portal authentication on the interface connected to the user. Then, the device uses static user information such as the user IP address as the user name for authentication.
Notes: After a static user is configured, the device preferentially uses the user name and password of the static user to authenticate the user when detecting that the user information matches the parameters such as the IP address range and domain name configured for the static user. If the authentication fails, the device performs 802.1X, MAC address, or Portal authentication on the user.
You can run the static-user username macaddress format command to specify the MAC address of a terminal as the user name and password for authentication, as well as the user name format. This command has a higher priority than the static-user username format-include and static-user password cipher password commands.
The static-user username format-include and static-user password commands are used to configure the user name and password of a static user respectively.
By default (the S5731 is used as an example):
  The user name of a static user is a combination of [system-name] and [ip-address]. For example, when the system name of an access device is huawei and the user IP address is 1.1.1.1, then the static user name is huawei1.1.1.1.
  The password of a static user is not configured.

## Slide 45: Applying NAC
An authentication profile is used to manage NAC configurations in a unified manner. To enable NAC, apply an authentication profile to an interface or VAP profile. This implements access control on users connected to the corresponding interface or VAPs.
The authentication method for users is determined by the access profile bound to the authentication profile.
[Huawei-GigabitEthernet0/0/1] authentication-profile authentication-profile-name
Apply the configured authentication profile. The following uses GE0/0/1 as an example.
The authentication-profile command applies an authentication profile to an interface or VAP profile.
By default, no authentication profile is applied to an interface or VAP profile. Different types of interfaces or VAP profiles may support different NAC functions. For details, see the product documentation.
Enter the interface view or VAP profile view.

## Slide 46: Configuration Example: Networking Requirements and Authentication Planning
Networking requirements
To enhance network security, an enterprise requires that all terminals (such as PCs, printers, and IP phones) be authenticated before accessing the network.
The enterprise network has the following characteristics:
Access switches do not support 802.1X authentication.
The enterprise network is small in scale and does not have any branches.
The enterprise has no more than 1000 employees. A maximum of 2000 terminals, including guest terminals, access the network every day.
Dumb terminals, such as IP phones and printers, are connected to the enterprise network.
Authentication planning
Deploy 802.1X authentication control points on the aggregation switch.
Deploy MAC address authentication for access of dumb terminals.
The authenticated users can access the intranet server cluster.
GE0/0/1
GE0/0/2
GE0/0/3
Campus egress
Intranet
SW1
SW2
SW3
SW4
Authentication server
192.168.100.100
Intranet server cluster
192.168.101.0/24
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/2
GE0/0/3
GE0/0/1

## Slide 47: Configuration Example: Data Plan
Item | Data
RADIUS server | IP address: 192.168.100.100
Intranet server cluster | Network segment: 192.168.101.0/24
Aggregation switch (SW2) | VLAN to which the uplink interface GE0/0/3 belongs: VLAN 100 VLAN to which downlink interfaces GE0/0/1 and GE0/0/2 belong: VLAN 200
Access switches (SW3 and SW4) | User VLAN ID: 200
RADIUS scheme | Authentication server IP address: 192.168.100.100 Authentication server port number: 1812 Accounting server IP address: 192.168.100.100 Accounting server port number: 1813 Shared key of the RADIUS server: Huawei@123 Authentication domain: nac
ACL number of the post-authentication domain | 3001

## Slide 48: Configuration Example: Procedure (1)
[SW3] l2protocol-tunnel user-defined-protocol 802.1X protocol-mac 0180-c200-0003 group-mac 0100-0000-0002
[SW3] interface gigabitethernet 0/0/1
[SW3-GigabitEthernet0/0/1] l2protocol-tunnel user-defined-protocol 802.1X enable
[SW3-GigabitEthernet0/0/1] bpdu enable
[SW3-GigabitEthernet0/0/1] quit
[SW3] interface gigabitethernet 0/0/2
[SW3-GigabitEthernet0/0/2] l2protocol-tunnel user-defined-protocol 802.1X enable
[SW3-GigabitEthernet0/0/2] bpdu enable
[SW3-GigabitEthernet0/0/2] quit
[SW3] interface gigabitethernet 0/0/3
[SW3-GigabitEthernet0/0/3] l2protocol-tunnel user-defined-protocol 802.1X enable
[SW3-GigabitEthernet0/0/3] bpdu enable
[SW3-GigabitEthernet0/0/3] quit
Enable network connectivity.
Configure transparent transmission of 802.1X packets. SW3 is used as an example.
GE0/0/1
GE0/0/2
GE0/0/3
Campus egress
Intranet
SW1
SW2
SW3
SW4
Authentication server
192.168.100.100
Intranet server cluster
192.168.101.0/24
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/2
GE0/0/3
GE0/0/1
Notes: In this example, SW3 and SW4 are deployed between the authentication switch SW2 and users. Therefore, transparent transmission of 802.1X packets must be configured on SW3 and SW4 so that SW2 can perform 802.1X authentication on users.

## Slide 49: Configuration Example: Procedure (2)
[SW2] aaa
[SW2-aaa] authentication-scheme a1
[SW2-aaa-authen-a1] authentication-mode radius
[SW2-aaa-authen-a1] quit
[SW2-aaa] accounting-scheme a2
[SW2-aaa-accounting-a2] accounting-mode radius
[SW2-aaa-accounting-a2] quit
[SW2-aaa] domain nac
[SW2-aaa-domain-nac] authentication-scheme a1
[SW2-aaa-domain-nac] accounting-scheme a1
[SW2-aaa-domain-nac] radius-server rd1
[SW2-aaa-domain-nac] quit
[SW2-aaa] quit
Configure a RADIUS server template.
Configure an AAA authentication scheme, accounting scheme, and an authentication domain.
[SW2] radius-server template rd1
[SW2-radius-rd1] radius-server authentication 192.168.100.100 1812
[SW2-radius-rd1] radius-server accounting 192.168.100.100 1813
[SW2-radius-rd1] radius-server shared-key cipher Huawei@123
[SW2-radius-rd1] quit
GE0/0/1
GE0/0/2
GE0/0/3
Campus egress
Intranet
SW1
SW2
SW3
SW4
Authentication server
192.168.100.100
Intranet server cluster
192.168.101.0/24
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/2
GE0/0/3
GE0/0/1

## Slide 50: Configuration Example: Procedure (3)
[SW2] mac-access-profile name m1
[SW2-mac-access-profile-m1] mac-authen username macaddress
[SW2-mac-access-profile-m1] quit
Configure an 802.1X access profile.
Configure a MAC access profile.
[SW2] dot1x-access-profile name d1
[SW2-dot1x-access-profile-d1] dot1x authentication-method eap
[SW2-dot1x-access-profile-d1] quit
[SW2] authentication-profile name p1
[SW2-authen-profile-p1] mac-access-profile m1
[SW2-authen-profile-p1] dot1x-access-profile d1
[SW2-authen-profile-p1] access-domain nac force
[SW2-authen-profile-p1] quit
Configure an authentication profile.
GE0/0/1
GE0/0/2
GE0/0/3
Campus egress
Intranet
SW1
SW2
SW3
SW4
Authentication server
192.168.100.100
Intranet server cluster
192.168.101.0/24
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/2
GE0/0/3
GE0/0/1

## Slide 51: Configuration Example: Procedure (4)
[SW2] acl 3001
[SW2-acl-adv-3001] rule 1 permit ip destination 192.168.101.0 0.0.0.255
[SW2-acl-adv-3001] rule 2 deny ip destination any
[SW2-acl-adv-3001] quit
Apply the authentication profile to interfaces.
Configure the authorized ACL to be delivered upon successful user authentication.
[SW2] interface gigabitethernet 0/0/1
[SW2-Gigabitethernet0/0/1] authentication-profile p1
[SW2-Gigabitethernet0/0/1] quit
[SW2] interface gigabitethernet 0/0/2
[SW2-Gigabitethernet0/0/2] authentication-profile p1
[SW2-Gigabitethernet0/0/2] quit
Create user accounts on the RADIUS server and configure corresponding rights.
GE0/0/1
GE0/0/2
GE0/0/3
Campus egress
Intranet
SW1
SW2
SW3
SW4
Authentication server
192.168.100.100
Intranet server cluster
192.168.101.0/24
GE0/0/1
GE0/0/2
GE0/0/3
GE0/0/2
GE0/0/3
GE0/0/1

## Slide 52
Overview of NAC
User Authentication Technologies
User Authorization and Logout
NAC Configuration
Policy Association

## Slide 53: Technical Background (1)
Deploying authentication at the access layer helps implement fine-grained permission management and high network security. As the network scale expands, some problems emerge.
Problems faced when access devices are used as authentication points
A large number of devices are deployed at the access layer, causing heavy configuration workload and difficult O&M.
The large number of access devices increases the load of the AAA server.
Users must access the network at fixed locations.
Aggregation layer
Access layer
Core layer
Authentication points

## Slide 54: Technical Background (2)
One solution is to move user authentication points from the access layer to the aggregation or core layer. In this way, authentication information on the entire network is centralized, the number of authentication points is greatly reduced, and the configuration and maintenance workload is reduced.
Problems faced when authentication points are moved upwards
Devices at the access layer must transparently transmit BPDUs. Otherwise, 802.1X authentication fails.
Authentication points cannot control mutual access between users in the same VLAN on an access device.
An administrator does not know the access positions of users, making fault locating difficult.
The gateway cannot detect user logout in real time.
Aggregation layer
Access layer
Core layer
Authentication points
Notes: Devices at the access layer must transparently transmit BPDUs. Otherwise, 802.1X authentication fails. The reason is as follows:
  EAP packets transmitted in 802.1X authentication are BPDUs. By default, Huawei switches do not perform Layer 2 forwarding for BPDUs. If a Layer 2 switch exists between the 802.1X-enabled device and users, Layer 2 transparent transmission must be enabled on the Layer 2 switch. Otherwise, the EAP packets sent by users cannot reach the 802.1X-enabled device, causing authentication failures.

## Slide 55: Overview of Policy Association
Policy association provides a solution to contradiction between policy strengths and complexity on large campus networks. In the solution, user access policies are centrally managed on the gateway and executed by the gateway and access devices.
A Control And Provisioning of Wireless Access Points (CAPWAP) tunnel is established between an authentication control point and an authentication execution point.
Authentication control devices and authentication access devices use CAPWAP tunnels to associate users, transmit messages, deliver user authorization policies, and synchronize user information.
Roles in the policy association solution
Terminals: provide human-machine interfaces for user authentication and resource access. The terminals include PCs, laptops, tablets, and dumb terminals.
Authentication access device: an authentication execution point that executes network access policies for users.
Authentication control device: an authentication control point that authenticates users and controls their access policies.
Authentication control point
Authentication execution point
CAPWAP tunnel
Terminals
Authentication access devices
Authentication control devices
Notes: After policy association is configured, access devices can transparently transmit BPDUs and report user logout and user access positions in real time. In addition, authentication control devices request authentication access devices to execute user access policies, thus controlling user access to the network.
Roles involved in policy association:
  Authentication access device: an authentication execution point that executes network access policies for users. When an authenticated user accesses the network, the device executes the corresponding access policy, such as a policy defining the VLAN, ACL, or UCL group to which the user belongs.
  Authentication control device: an authentication control point that authenticates users and controls their access policies. The device authenticates the identities of users who attempt to access the network and specifies their network access rights, that is, accessible resources.

## Slide 56: Implementation of Policy Association
User
Authentication execution point
(access device)
Authentication control point
(control device)
A user accesses the network.
Establish a CAPWAP tunnel.
Send a user association request.
Send a user association response.
5. Perform user authentication.
Send a user authorization request.
Send a user authorization response.
The user starts to access resources.
Typical scenarios of policy association
User access: When a user accesses the network, the authentication execution point creates a user association entry. The user and authentication control point exchange authentication information. After the authentication is successful, the authentication control point delivers authorization information to the authentication execution point.
User logout: When a user is disconnected from the access device, the authentication execution point notifies the authentication control point of the user logout through the CAPWAP tunnel in real time. The authentication control point then deletes the user entry.
User movement: When a user moves and connects to a new network, the user is re-authenticated.
Notes: User login process:
  The control device and access device establish a CAPWAP tunnel with each other.
  When detecting the access of a new user, the access device creates a user association entry to record basic information such as the user and access interface.
  The access device sends a user association request to the control device.
  The control device creates a user association entry to save the mapping between the user and access device, and returns a user association response to notify the access device of successful association.
  The user initiates an authentication request to the control device. The access device forwards the authentication packets between the user and control device.
  The control device deletes the user association entry. When the authentication succeeds, the control device generates a complete user entry, and sends a user authorization request to the access device, and delivers the network access policy of the user to the access device.
  The access device updates the user association entry, grants the specified network access rights to the user, and sends a user authorization response to the control device.
  The user accesses the specified network resources.

## Slide 57: Comparison Between Policy Association and Authentication
Interface
Authentication module
Interface
Authentication execution point
Authentication control point
User
Authentication server
User
Authentication server
Authentication point
Send the user credential.
CAPWAP tunnel
Send the user credential.
1
1
2
3
2
3
Forward the user credential to the authentication server.
4
Transmit the user credential through a CAPWAP tunnel.
Transmit the user credential to the authentication module.
Transmit the user credential to the authentication module.
Forward the user credential to the authentication server.
Authentication
Policy association
Authentication module
Policy execution interface
Interface
Policy execution interface
Notes: Authentication:
  The user exchanges information with the authentication point. The authentication point directly exchanges authentication information with the authentication server. When the authentication succeeds, the authentication server delivers the user rights to the authentication point. The interface on the authentication point then executes the corresponding user policy.
Policy association:
  The user exchanges information with the authentication execution point. The authentication execution point transmits the user credential to the authentication control point through a CAPWAP tunnel. The authentication control point exchanges authentication information with the authentication server.
  When the authentication succeeds, the authentication server delivers user rights to the authentication control point, which further forwards the user rights to the authentication execution point through the CAPWAP tunnel. Finally, the interface on the authentication execution point executes the corresponding user policy.

## Slide 58: Policy Association Configuration Roadmap
Policy association controls network access of users. Before configuring policy association, complete the following tasks:
Configure the user access authentication mode.
802.1X, MAC, or Portal
1
Configure user authentication, authorization, and accounting.
Authentication mode
User authorization
...
2
Configure an access device.
Establish a CAPWAP tunnel.
Configure an interface as an access point.
Configure a control device.
Establish a CAPWAP tunnel.
Configure an interface as a control point.
Configure access authentication for access devices.
Configure user authorization information.
Policy association needs to be configured on both control devices and access devices in any sequence.

## Slide 59: Policy Association Configuration: Configuring an Access Device
[Huawei] as access interface vlanif vlan-id
Establish a CAPWAP tunnel.
The source interface for establishing a CAPWAP tunnel is configured on the access device.
[Huawei-GigabitEthernet0/0/1] authentication access-point [ open ]
Configure an interface as the access point (authentication execution point).
Remote access control is enabled on an interface of the access device.
[Huawei] as access controller ip-address ip-address
The IP address of a control device is configured on the access device.
Notes: [Huawei-GigabitEthernet0/0/1] authentication access-point [ open ]
  open: Disables right control of the access point.

## Slide 60: Policy Association Configuration: Configuring a Control Device (1)
[Huawei] capwap source interface { loopback loopback-number | vlanif vlan-id }
Establish a CAPWAP tunnel.
The source interface for establishing a CAPWAP tunnel is configured on the control device.
[Huawei-GigabitEthernet0/0/1] authentication control-point [ open ]
Configure an interface as the authentication control point.
An interface on the control device is configured as the authentication control point.
Configure access authentication for access devices.
[Huawei] as-auth
The access device authentication view is displayed.
[Huawei-as-auth] auth-mode none
The access device authentication mode is set to none authentication.
Notes: [Huawei-GigabitEthernet0/0/1] authentication control-poin [ open ]
  open: Enables the forwarding function of the control point.
Configure access authentication for access devices.
  By default, access devices can connect to a control device only after passing authentication. The control device authenticates access devices using a blacklist and whitelist. Blacklisted access devices cannot connect to the control device, whereas whitelisted access devices can. The control device does not authenticate access devices out of the blacklist and whitelist, and you need to manually specify allowed access devices. You can also configure none authentication for access devices. As a result of this configuration, an access device can connect to the control device regardless of whether the access device is in the blacklist or whitelist.
  For details about how to configure this function, see the product documentation.

## Slide 61: Policy Association Configuration: Configuring a Control Device (2)
[Huawei-aaa] service-scheme service-scheme-name
Configure user authorization information to be delivered to the access device and control device.
A service scheme is created and the service scheme view is displayed.
[Huawei-aaa-service-huawei] remote-authorize { acl | car | ucl-group }
User authorization information to be delivered to the access device is configured.
[Huawei-aaa-service-huawei] local-authorize { none | { acl | car | priority | ucl-group | vlan } }
User authorization information to be delivered to the control device is configured.

## Slide 62: Configuration Example: Networking Requirements and Authentication Planning
Networking requirements
Large campus networks have many access devices, so user access policy deployment is time-consuming and the policies are difficult to modify.
The customer requires that NAC authentication and user access policies be configured on the gateway and the access policies be executed on access devices to simplify device deployment at the access layer.
Authentication planning
Configure the gateway SW1 as the control device and SW2 as the access device.
Configure the control device to authenticate users and the access device to execute user access policies.
Configure VLAN 10 as the user VLAN and VLAN 20 as the management VLAN of the CAPWAP tunnel. In this example, 802.1X authentication is used.
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 63: Configuration Example: Data Plan
Item | Data
RADIUS server | IP address: 192.168.4.30
Gateway switch (control device, SW1) | VLAN to which the uplink interface GE0/0/3 belongs: VLAN 30 VLAN to which downlink interface GE0/0/1 belongs: VLAN 10 (user VLAN), VLAN 20 (management VLAN)
Access switch (SW2) | VLAN to which users belong: VLAN 10
RADIUS scheme | Authentication server IP address: 192.168.4.30 Authentication server port number: 1812 Shared key of the RADIUS server: Huawei@123 Authentication domain: nac
ACL number of the post-authentication domain | 3001
Access permission | Prohibit access to resources on the 192.168.5.0/24 network segment.

## Slide 64: Configuration Example: Procedure (1)
Create VLANs and configure the allowed VLANs on interfaces.
On the control device, configure an interface address pool on VLANIF 10 to assign IP addresses to users.
[SW1] dhcp enable
[SW1] interface vlanif 10
[SW1-Vlanif10] ip address 192.168.1.1 255.255.255.0
[SW1-Vlanif10] dhcp select interface
[SW1-Vlanif10] quit
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 65: Configuration Example: Procedure (2)
[SW1] interface vlanif 20
[SW1-Vlanif20] ip address 192.168.2.1 255.255.255.0
[SW1-Vlanif20] dhcp select interface
[SW1-Vlanif20] dhcp server option 43 ip-address 192.168.2.1
[SW1-Vlanif20] quit
[SW1] capwap source interface vlanif 20
[SW1] as-auth
[SW1-as-auth] auth-mode none
[SW1-as-auth] quit
Configure the control device and access device to establish a CAPWAP tunnel.
[SW2] interface vlanif 20
[SW2-Vlanif20] ip address dhcp-alloc
[SW2-Vlanif20] quit
[SW2] as access interface vlanif 20
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 66: Configuration Example: Procedure (3)
[SW1] radius-server template rd1
[SW1-radius-rd1] radius-server authentication 192.168.4.30 1812
[SW1-radius-rd1] radius-server shared-key cipher Huawei@123
[SW1-radius-rd1] quit
[SW1] aaa
[SW1-aaa] authentication-scheme abc
[SW1-aaa-authen-abc] authentication-mode radius
[SW1-aaa-authen-abc] quit
[SW1] domain nac
[SW1-aaa-domain-isp1] authentication-scheme abc
[SW1-aaa-domain-isp1] radius-server rd1
[SW1-aaa-domain-isp1] quit
[SW1-aaa] quit
On the control device, create and configure a RADIUS server template, an AAA authentication scheme, and an authentication domain.
[SW1] domain nac
# Configure a global default domain named nac.
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 67: Configuration Example: Procedure (4)
[SW1] interface gigabitethernet 0/0/1
[SW1-GigabitEthernet0/0/1] authentication control-point
[SW1-GigabitEthernet0/0/1] quit
[SW2] interface gigabitethernet 0/0/2
[SW2-GigabitEthernet0/0/2] authentication access-point
[SW2-GigabitEthernet0/0/2] quit
[SW2] interface gigabitethernet 0/0/3
[SW2-GigabitEthernet0/0/3] authentication access-point
[SW2-GigabitEthernet0/0/3] quit
Configure the control device as the control point and the access device as the access point.
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 68: Configuration Example: Procedure (5)
[SW1] aaa
[SW1-aaa] service-scheme asd
[SW1-aaa-service-asd] remote-authorize acl
[SW1-aaa-service-asd] quit
[SW1-aaa] domain nac
[SW1-aaa-domain-nac] service-scheme asd
[SW1-aaa-domain-nac] quit
[SW1-aaa] quit
Configure the control device to deliver ACL-based authorization information to the access device, and bind the AAA service scheme asd to the authentication domain nac.
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 69: Configuration Example: Procedure (6)
[SW1] acl 3001
[SW1-acl-adv-3001] rule deny ip destination 192.168.5.0 0.0.0.255
[SW1-acl-adv-3001] quit
Configure ACLs and ACL rules for authorization on the control device and access device.
[SW2] acl 3001
[SW2-acl-adv-3001] rule deny ip destination 192.168.5.0 0.0.0.255
[SW2-acl-adv-3001] quit
Configure 802.1X authentication on the control device and access device, and configure an authentication-free rule on the control device to allow packets from the management VLAN of the CAPWAP tunnel to pass through. (The 802.1X authentication configuration is not mentioned here.)
[SW1] free-rule-template name default_free_rule
[SW1-free-rule-default_free_rule] free-rule 1 source vlan 20
[SW1-free-rule-default_free_rule] quit
GE0/0/1
GE0/0/3
Intranet
SW1 (gateway)
SW2 (access)
RADIUS Server
192.168.4.30
GE0/0/1
GE0/0/2
GE0/0/3
VLAN 10
VLAN 10, VLAN 20
VLAN 30
User VLAN: VLAN 10
Management VLAN: VLAN 20

## Slide 70
(Single-answer question) When PCs and dumb terminals such as printers and fax machines are connected to an interface of an access device, which authentication mode can be used to ensure network security and allow dumb terminals to access the network? ( )
  MAC address authentication
  802.1X authentication
  Portal authentication
  MAC address bypass authentication
Notes: D

## Slide 71
(Multiple-answer question) Based on which of the following can a Huawei device deliver user access rights to a successfully authenticated user? ( )
  VLAN
  IP address
  ACL
  UCL group
Notes: ACD

## Slide 72
User access control is the first line of defense to protect a network, where you can deploy user authentication, such as MAC address authentication, 802.1X authentication, and Portal authentication, to ensure security.
The implementation modes and application scenarios of these technologies are different. You need to select and deploy them based on network characteristics and requirements.
iMaster NCE-Campus can be used together with network products to provide an advanced NAC solution that implements powerful functions such as terminal type identification and policy automation.