## Slide 1
Datacom
General
V1.0
Zhu Shigeng/00261992
2019.11.25
Yao Ning/00276205 & Wan Yunfei/00364921
New
Lu Yueyue/WX445705
2020.10.27
Yao Ning/00276205
Update
Lu Yueyue/WX445705
2021.07.15
Wu Yue/WX291773
Update

## Slide 2: Free Mobility

## Slide 3
On a campus network, different network access policies can be deployed for users on access devices to meet diverse network access requirements.
On a traditional campus network, users' network access rights are controlled using the Network Admission Control (NAC) technology, in conjunction with VLAN and ACL technologies. However, this solution has many defects. For example, the association between ACLs and users takes effect only on authentication points, resulting in poor flexibility; VLANs and ACLs need to be configured on a large number of switches that function as authentication points in advance, causing a heavy deployment and maintenance workload.
Mobile working requires that these defects be removed and employees access the network from any place, any VLAN, or any IP network segment with controlled network access rights. To implement these, the free mobility solution is introduced.

## Slide 4
On completion of this course, you will be able to:
  Describe the requirements of large-scale campus networks for policy control.
  Describe the differences between free mobility and traditional technologies or solutions.
  Describe the basic functions and working mechanism of free mobility.
  Understand the relationship between free mobility and campus network access authentication.
  Describe the typical application solution of free mobility.

## Slide 5
Technical Background and Basic Concepts of Free Mobility
Working Mechanism of Free Mobility
Free Mobility Solution Design

## Slide 6: Mobility Requirements of Users on the Network
User A
User A
Move
Scenario description
User mobility requirements, such as mobile working, are common on large-scale campus networks.
To ease campus network management, it is required that users obtain the same network access policy regardless of their locations and IP addresses.
Solution challenges
How to ensure that users can access the campus network from any place?
How to ensure the security of user access to the campus network?
Can user information be managed in a centralized manner?
Are the network configuration and configuration delivery simple enough?
Is it easy to adjust policies?
Notes: With the construction and promotion of wireless networks, the boundaries of enterprise campus networks are disappearing, and office locations of enterprise employees become more flexible.
The large-scale movement of employees' access locations improves enterprise production efficiency, but also brings challenges to enterprise network management and security. Mobile working causes the IP addresses of employees' hosts to change frequently. However, traditional campus networks cannot adapt to this change because employees' rights are controlled based on their IP addresses.

## Slide 7: Traditional Solution: Using NAC Together with VLANs and ACLs
On a traditional campus network, users' network access rights are controlled using the NAC technology together with VLANs and ACLs. However, this solution has the following defects.
The deployment and maintenance workload is heavy.
VLANs and ACLs need to be configured on a large number of switches that function as authentication points in advance.
The association between ACLs and users takes effect only on authentication points.
For non-authentication points, policies must be configured based on IP addresses.
ACLs need to be configured in advance.
At least the range of destination IP addresses to which users are permitted or denied access must be defined in ACLs.
Therefore, if IP addresses of users are not fixed, ACLs are not suitable for controlling traffic sent from or destined for these users.
Employees are required to access the network and go online through a specified switch, VLAN, or network segment.
Notes: Mobile working requires that these defects be removed and employees obtain consistent network access rights when accessing the network from any place, any VLAN, or any IP network segment. In addition, administrators want to have a simple policy control approach that is decoupled from network topologies and IP addresses.

## Slide 8: Overview of Free Mobility
The free mobility solution allows a user to obtain the same network access policy regardless of the user's location and IP address on a campus network. iMaster NCE-Campus and switches work together to enable network access rights to automatically move with users, improving mobile working experience.
Free mobility resolves the problems faced by traditional campus networks in three aspects
Decoupling of service policies from IP addresses.
Centralized management of user information.
Centralized policy management.
Advantages of free mobility
Simplified network planning: Administrators no longer need to consider user IP addresses when configuring policies.
Enhanced control capability: User authentication information can be synchronized between network devices.
Improved management efficiency: Administrators no longer need to configure devices one by one.
User A
User A
Move
Free mobility
Notes: Decoupling of service policies from IP addresses
  Using iMaster NCE-Campus, administrators can divide users and resources on the entire network into different security groups based on diverse dimensions. In addition, network devices in the free mobility solution use an innovative software and hardware design. Such a device can match source and destination security groups based on the source and destination IP addresses of packets, and then find the matching inter-group policy based on these security groups.
  Through the innovative designs, all the user- and IP address–based service policies on traditional networks can be transformed into security group–based policies. When predefining service policies, administrators no longer need to consider user IP addresses. This achieves decoupling of service policies from IP addresses.
Centralized management of user information
  Administrators can use iMaster NCE-Campus to centrally manage user authentication and login information and obtain the mappings between network-wide users and their IP addresses.
Centralized policy management
  iMaster NCE-Campus is not only the authentication center on a campus network, but also the management center of service policies. Administrators can use iMaster NCE to centrally manage service policies on policy enforcement devices on the entire network. After being configured for once, service policies can be automatically delivered to policy enforcement devices on the campus network. These policies include permission control policies (for example, group A is forbidden to access group B) and experience guarantee policies (for example, the bandwidth and priority for forwarding traffic of group A are controlled).

## Slide 9: Implementation of Free Mobility
Free mobility implements policy management and permission control based on security groups.
Campus network
User A
User B
User C
NAC
NAC
NAC
Deliver security groups and policies
3
4
2
Sales user
security group
R&D user
security group
Server resource
security group
Permission control policies
1
Security groups are defined, each representing a group of users who have the same network access requirements.
Permission control policies are defined based on security groups and are delivered to network devices.
Users obtain authorized security groups after they are successfully authenticated.
After user traffic enters a network, network devices enforce policies based on the source and destination security groups of the traffic.
Notes: Free mobility introduces the concept of security group. Security groups are related only to user identities and are completely decoupled from network information such as user VLANs and IP addresses.
User policy management and permission control are implemented based on security groups.

## Slide 10: Traditional Solution vs. Free Mobility Solution
Customer Requirement | Traditional Solution | Free Mobility Solution
Consistent network access rights in the mobile working scenario | The "dynamic VLAN + static ACL" solution is used. The configuration planning is complex, the pre-configuration workload is heavy, ACL maintenance is difficult, and consistent network access rights cannot be ensured for users. | Network access policies are decoupled from IP addresses. Administrators divide security groups based on user identities on iMaster NCE-Campus, and use a policy control matrix to manage policies in a unified manner. This simplifies configuration and maintenance, and ensures that users can obtain the same network access rights as they move.
Service-based user isolation | The "Layer 2 VLAN isolation + Layer 3 ACL isolation" solution is used. In the mobile working scenario, the configuration planning is complex, the pre-configuration workload is heavy, ACL maintenance is difficult, and user isolation is hard to implement. | The "Layer 2 port isolation + inter-group isolation based on security groups" solution is used. Inter-group isolation policies are decoupled from IP addresses, simplifying configuration and maintenance and effectively achieving user isolation.
Simplified configuration and management | A large number of rules such as VLANs and ACLs need to be planned based on IP addresses during network design. These rules are complex to configure and difficult to understand, causing inconvenience in subsequent maintenance. | Based on security groups (UCL groups), only several user groups and inter-group policies need to be defined, greatly simplifying planning and configuration. In addition, the policy control matrix is easy to understand and maintain.

## Slide 11: Basic Concepts in Free Mobility: Authentication and Policy Enforcement
Core
Authentication point
Access
Policy control center
Authentication point: authenticates terminals and obtains authorization results (containing the security groups to which terminals belong) from iMaster NCE-Campus.
iMaster NCE-Campus: serves as the authentication server and the policy control center to maintain the policy control matrix, which defines policies for controlling access between network-wide security groups.
Core
Policy enforcement point
Access
Policy enforcement point: obtains the policy control matrix from iMaster NCE-Campus, and enforces policies based on the source and destination security groups to which the source and destination IP addresses of the received traffic belong. If the policy allows the traffic to pass through, the policy enforcement point forwards the traffic. Otherwise, the traffic is dropped.
User A
User B
User A
User B
Authentication
Authentication
Policy enforcement
Notes: Additional information about the policy enforcement point:
  The policy enforcement point is responsible for enforcing security group–based service policies. To enforce these policies, the policy enforcement point must be able to identify the source and destination security groups of packets. It can obtain the mappings between IP addresses and security groups during the authentication process or from iMaster NCE-Campus.
  The authentication point and policy enforcement point are two device roles. Based on the administrator's configuration and device capabilities, a physical device can play either or both of the two roles.

## Slide 12: Basic Concepts in Free Mobility: Security Group (1)
A security group is an abstracted and logical set of communicating objects on a network.
An administrator can add the users requiring the same access control policy to the same security group, and configure an access control policy for the group.
Classification of security groups
Security group members can be network terminals such as PCs and smartphones. They can be added by an administrator or dynamically added upon successful authentication.
  Static security group: It is a security group defined by statically binding IP addresses.
  Dynamic security group: Users who meet specified conditions are authorized a specific security group.
A dynamic security group has a higher priority than a static security group. For example, a user with IP address 1 is statically bound to security group 1, and the user is dynamically added to security group 2 upon successful RADIUS authentication. Eventually, the user belongs to security group 2.
Special security groups
Unknown (default): Users or resources that are not dynamically or statically added to any security group belong to this group by default.
Any (default): All users and resources belong to this group. It is typically used to configure default rules, and can be configured as the destination group only.
Bypass security group (user-defined): When the IP-security group channel between the policy enforcement point and iMaster NCE-Campus is disconnected, unknown traffic is controlled based on the policy configured for the bypass security group. Only one bypass security group can be configured, and members must be statically added to this group.
Notes: Security group:
  An administrator can define security groups on iMaster NCE-Campus to describe and organize the sources or destinations of network traffic, and then configure policies to control mutual access between the security groups.
  An administrator can add network objects that have the same access requirements to the same security group, and configure a policy for this security group. In this way, these network objects obtain the same permissions as configured for the security group. For example, an administrator can define the following security groups: R&D group (a collection of individual hosts), printer group (a collection of printers), and database server group (a collection of server IP addresses and ports). Compared with the solution in which access control policies are deployed for each user, the security group–based access control solution greatly reduces the administrator's workload.

## Slide 13: Basic Concepts in Free Mobility: Security Group (2)
Campus network
Sales
group
Guest
group
Host 1
Sales user
802.1X
Host 2
Sales user
MAC
Host 3
Guest
Portal
Server
group
Dynamic security groups
Static security groups
Dynamic security group
The IP addresses of users in dynamic security groups are not fixed, and are dynamically bound to security groups after the users are authenticated. After users log out, the bindings are dynamically canceled. These mappings remain valid only when users are online.
Network devices can obtain such mappings from iMaster NCE-Campus or when they function as authentication points.
Static security group
IP addresses of static resources are fixed, and are statically bound to security groups by an administrator through configuration.
In the pre-deployment phase, when iMaster NCE-Campus is used to deploy control policies on network devices through NETCONF, iMaster NCE-Campus will synchronize the bindings between security groups and IP addresses to all policy enforcement points.
Group Type | Group Name | Group ID
Dynamic | Sales | 1
Dynamic | Guest | 2
Static | Server | 3
Notes: Classification of security groups:
  A security group can be both a dynamic security group and a static security group. That is, it is bound to both multiple authorization rules to represent dynamic users and multiple IP addresses or IP network segments to represent static resources. The differences are as follows:
    The IP addresses of users in dynamic security groups are not fixed, and are dynamically bound to security groups after the users are authenticated. After users log out, the bindings are dynamically canceled. These mappings remain valid only when users are online. Network devices can obtain the mappings between IP addresses and security groups (also known as IP-security group entries) by acting as authentication points, or iMaster NCE-Campus delivers the mappings to network devices.
    The IP addresses of static resources are fixed. An administrator needs to bind these IP addresses to static security groups on iMaster NCE-Campus, which then synchronizes the bindings to policy enforcement points. Static security group members can be any network objects that use fixed IP addresses, such as terminals, servers, interfaces of network devices, and authentication-free users.
  If an IP address is added to different groups both in static mode and upon successful authentication, the dynamic security group assigned during authentication takes effect.
  An IP address can belong to only one security group.

## Slide 14: Basic Concepts in Free Mobility: UCL Group
User Control List (UCL) group:
  UCL groups identify user types. An administrator can add the users requiring the same network access policy to the same UCL group, and configure a network access policy for the group. Compared with the solution in which network access policies are deployed for each user, the UCL group–based access control solution greatly reduces the administrator's workload.
  A UCL group is called a security group on iMaster NCE-Campus.
UCL group configuration on a switch:
  Create a UCL group.
  Configure a static UCL group.
[Huawei] ucl-group ip ip-address { mask-length | ip-mask } { group-index | name group-name }
[Huawei] ucl-group group-index [ name group-name ]
Campus network
FTP server
Web server
Email server
Guests (UCL group)
Sales users (UCL group)

## Slide 15: Basic Concepts in Free Mobility: Resource Group
Disadvantages of security groups
Administrators can bind static IP addresses of servers to static security groups, and iMaster NCE-Campus delivers these bindings to devices through NETCONF.
However, such static security groups cannot distinguish different services that use the same IP addresses.
Resource group
is a way out
Resource group
IP addresses specified in resource groups can overlap.
During the configuration of the policy control matrix, a resource group can only be specified as the destination group (not a source group) of a policy.
When policies are delivered to switches, the policies are decomposed into corresponding IP addresses, instead of using the security group (UCL group) model.
Campus
network
192.168.1.1
Guests
HTTP server
DNS server
Group Type | Group Name | IP Address
Resource group | DNS | 192.168.1.1
Resource group | HTTP | 192.168.1.1
Resource groups:
The server with IP address 192.168.1.1 provides both DNS and HTTP services.
Resource groups can be deployed to distinguish the two types of services.
Notes: Dumb terminals, data center server resources, and authentication-free users do not need to be authenticated when accessing the network. Therefore, they cannot be authorized by the AAA server. In this case, you can bind their static IP addresses to resource groups.
Note: When resource groups are used, a policy enforcement point generates a policy by IP address, instead of based on each resource group. As such, the device may have a large number of policies.

## Slide 16: Basic Concepts in Free Mobility: Policy Control Matrix
After security groups are defined, administrators can define inter-group policies on the entire network.
A policy control matrix is used to configure inter-group policies to control access from source groups to destination groups.
Source Group | Sales | Guest | Server
Sales |  |  | 
Guest |  |  | 
Server |  |  | 
Campus network
FTP server
Web server
Email server
Guests (security group)
Sales users (security group)
Policy control matrix
Destination Group
Notes: When multiple policies are configured to control access from a source security group to multiple destination groups, an administrator needs to configure priorities of the policies to determine the sequence in which policies are matched. For example, if the destination groups are resource groups with overlapping IP addresses, the administrator can set a high priority for a policy so that the policy can be matched preferentially.
For unknown users:
  If a policy enforcement device does not find any security group corresponding to an IP address, it considers that the IP address belongs to the default security group named unknown, and enforces the matching security group policy (default policy: permit).
The following uses the traffic from the sales group to the server group as an example to describe policy matching in the policy control matrix:
  The device (policy enforcement point) first searches for the policy of controlling access from the sales group to the server group. If no such inter-group policy is found in the policy control matrix, the device continues matching policies.
  The device then searches for the policy of controlling access from the sales group to the any group. If no such inter-group policy is found in the policy control matrix, the device continues matching policies.
  Finally, the device matches traffic with the policy of controlling access from the any group to the any group. By default, this policy exists in the policy control matrix and defines the permit action. That is, traffic is permitted by default if no policy is matched.

## Slide 17: Basic Concepts in Free Mobility: IP-Security Group Entry Subscription
IP-security group entry subscription
If the authentication point and policy enforcement point are located on different devices, the IP-security group entries of authenticated users need to be pushed to the specified policy enforcement point.
An administrator can configure subscription on iMaster NCE-Campus to specify the entries of which network segments or security groups to be pushed to which policy enforcement points.
Subscription procedure
After the authentication point authenticates a user through the RADIUS server, the RADIUS server authorizes the corresponding security group and creates an IP-security group entry for the user.
The RADIUS server reports this IP-security group entry to the IP-security group component through an HTTP/2.0 channel, which then delivers this entry to specific policy enforcement points.
IP | Security Group
192.168.1.1 | Group1
192.168.2.1 | Group2
Core
Authentication Point
Access
Policy enforcement point
Policy control center
User A
192.168.1.1
User B
192.168.2.1
Authentication Point
Policy enforcement point
1. Identity authentication
2. IP-security
group entry push
IP-security group entry
Notes: A policy enforcement point can obtain IP-security group entries in either of the following ways:
  The policy enforcement point obtains IP-security group entries during user authentication when it is located on the same device as the authentication point.
  iMaster NCE-Campus pushes IP-security group entries to the policy enforcement point through an HTTP/2.0 channel. This scenario is known as IP-security group entry subscription.
In the IP-security group entry subscription scenario, iMaster NCE-Campus must have already generated IP-security group entries during user authentication. Therefore, IP-security group entry subscription has the following requirements:
  iMaster NCE-Campus functions as the RADIUS server to perform end user authentication. In this way, it can generate IP-security group entries during user authentication, and synchronize the entries to the free mobility component.
  iMaster NCE-Campus functions as a RADIUS relay agent when a third-party RADIUS server is used for user authentication. In this way, iMaster NCE-Campus can obtain security group information during the authentication process to generate IP-security group entries.

## Slide 18
Technical Background and Basic Concepts of Free Mobility
Working Mechanism of Free Mobility
Free Mobility Solution Design

## Slide 19: Working Mechanism of Free Mobility: Overview
Create users and security groups.
An administrator defines security groups on iMaster NCE-Campus.
The administrator creates user accounts on iMaster NCE-Campus, and configures authorization rules and results to bind the users to security groups.
Define and deploy a policy control matrix.
The administrator specifies a policy enforcement point on iMaster NCE-Campus and defines a policy control matrix.
iMaster NCE-Campus automatically delivers inter-group policies to the policy enforcement point.
A user initiates authentication.
A user accesses the network, and iMaster NCE-Campus verifies the user identity.
iMaster NCE-Campus associates the user with the corresponding security group based on the user login information, and delivers the authorization result containing the security group to which the user belongs to the authentication point.
The user accesses network resources.
The policy enforcement point identifies the source and destination groups of packets based on the mapping between the user's IP address and security group, and then matches and enforces an inter-group policy.
User terminal
Authentication point & policy enforcement point
An administrator defines user security groups and inter-group policies.
Deliver security groups and inter-group policies.
Initiate authentication.
Verify the user identity and associate the user with a security group.
Intranet
The user accesses network resources, and the policy enforcement point enforces the corresponding inter-group policy.
(In this example, the authentication point and policy enforcement point are located on the same device.)
Notes: Free mobility deployment based on iMaster NCE-Campus:
  Create users and security groups.
    An administrator can define users and security groups on iMaster NCE-Campus in a unified manner. Security groups can be defined based on network services for configuring inter-group control policies.
  Define and deploy a policy control matrix.
    The administrator defines inter-group policies in a policy control matrix on iMaster NCE-Campus, and delivers the policy control matrix to policy enforcement points.
  A user initiates authentication.
    When a user is being authenticated, iMaster NCE-Campus associates the user with a security group based on the user login information. After the user is authenticated successfully, iMaster NCE-Campus delivers the authorization result containing the security group to which the user belongs to the authentication point. During 802.1X authentication, if a terminal has not obtained an IP address, the authentication point automatically detects the actual IP address of the user after the user is successfully authenticated and obtains an IP address, and reports the user's actual IP address to iMaster NCE-Campus. iMaster NCE-Campus collects IP addresses of all online users and synchronizes all user information to policy enforcement points.

## Slide 20
Notes:     If the authentication point and policy enforcement point are located on different devices, the policy enforcement point needs to obtain the mappings between user IP addresses and security groups (that is, IP-security group entries) to identify the source and destination groups of traffic during policy enforcement. Therefore, the administrator needs to subscribe to the required IP-security group entries.
  The user accesses network resources.
    A user sends service traffic. When a packet reaches the policy enforcement point, the device identifies the security groups that match the source and destination IP addresses of the packet, and enforces the corresponding inter-group policy.

## Slide 21: Working Mechanism of Free Mobility (1)
Core
Firewall
User1
192.168.1.1/24
User2
192.168.2.1/24
Server
10.1.1.1/24
Group Type | Group Name | Group ID
Dynamic | Group1 | 1
Dynamic | Group2 | 2
Static | Server | 3
User | Password
User1 | ***
User2 | ***
Create users on iMaster NCE-Campus.
Create security groups, bind the server IP address to the server security group, and configure authorization rules and results to bind User1 and User2 to security groups Group1 and Group2, respectively.
Dynamic authorization (User1)
Dynamic authorization (User2)
Static binding <- 10.1.1.1/32 (server)

## Slide 22: Working Mechanism of Free Mobility (2)
Core
Firewall
User1
192.168.1.1/24
User2
192.168.2.1/24
Server
10.1.1.1/24
Source Group | Group1 | Group2 | Server
Group1 |  |  | 
Group2 |  |  | 
Server |  |  | 
Define a policy control matrix (inter-group policies) on iMaster NCE-Campus and specify the policy enforcement point device (Core).
Policy enforcement point
Destination Group
Notes: To manually specify a device as a policy enforcement point managed by iMaster NCE-Campus, enable the free mobility function by running the following command:
[HUAWEI] group-policy controller ip-address1 [ port-number1 ] password password [ src-ip ip-address2 ]
  ip-address1 [ port-number1 ]: specifies the IP address of a controller and the port number used by the device to exchange packets with the controller. If no port number is configured, the default port number 5222 is used.
  password password: specifies the password used by the device to connect to the controller. The password configured on the device must be the same as that configured on the controller.
  src-ip ip-address2: specifies the source IP address used by the device to communicate with the controller. If this parameter is not configured, the device selects one of its own IP addresses to communicate with the controller.

## Slide 23: Working Mechanism of Free Mobility (3)
Core
Firewall
User1
192.168.1.1/24
User2
192.168.2.1/24
Server
10.1.1.1/24
iMaster NCE-Campus pushes inter-group policies to the policy enforcement point.
Policy control matrix
Source Group | Group1 | Group2 | Server
Group1 |  |  | 
Group2 |  |  | 
Server |  |  | 
Destination Group
Policy enforcement point

## Slide 24: Working Mechanism of Free Mobility (4)
Core
Firewall
User1
192.168.1.1/24
MAC-X
User2
192.168.2.1/24
MAC-Y
Server
10.1.1.1/24
Policy enforcement point
Authentication Point
Authentication packets
1
2
3
Authorization result:
Group1
Online user entry
3
User1 attempts to access the network. The core switch functioning as the authentication point exchanges user authentication information with iMaster NCE-Campus.
iMaster NCE-Campus checks the login information of User1 and associates User1 with the corresponding security group (Group1) in the authorization policy.
After User1 is authenticated, iMaster NCE-Campus associates the user IP address with Group1 and records the association in an IP-security group entry. In addition, the iMaster NCE-Campus notifies the authentication point of the security group to which the user belongs, and the core device at the authentication point generates an online user entry.
The preceding process also applies to User2.
After receiving a service packet from a terminal, the core switch that also functions as the policy enforcement point identifies the security group that matches the source and destination IP addresses of the packet and enforces the corresponding inter-group policy.
MAC | IP | Security Group
MAC-X | 192.168.1.1 | Group1

## Slide 25: Working Mechanism of Free Mobility (5)
IP packet
Source: 192.168.1.1
Destination: 192.168.2.1
5
Discard
Online user entry
MAC | IP | Security Group
MAC-X | 192.168.1.1 | Group1
MAC-Y | 192.168.2.1 | Group2
Policy (permission control):
4
Core
Firewall
User1
192.168.1.1/24
MAC-X
User2
192.168.2.1/24
MAC-Y
Policy enforcement point
Authentication Point
User1 attempts to access the network. The core switch functioning as the authentication point exchanges user authentication information with iMaster NCE-Campus.
iMaster NCE-Campus checks the login information of User1 and associates User1 with the corresponding security group (Group1) in the authorization policy.
After User1 is authenticated, iMaster NCE-Campus associates the user IP address with Group1 and records the association in an IP-security group entry. In addition, the iMaster NCE-Campus notifies the authentication point of the security group to which the user belongs, and the core device at the authentication point generates an online user entry.
The preceding process also applies to User2.
After receiving a service packet from a terminal, the core switch that also functions as the policy enforcement point identifies the security group that matches the source and destination IP addresses of the packet and enforces the corresponding inter-group policy.
Source Group | Destination Group | Action
Group1 | Group2 | Deny
Group1 | Server | Permit
... | ... | ...

## Slide 26
Technical Background and Basic Concepts of Free Mobility
Working Mechanism of Free Mobility
Free Mobility Solution Design

## Slide 27: Security Group Design
Dynamic security group (users)
Users and terminals that can access the network only after being authenticated.
  In most cases, dynamic security groups can be defined based on user identities, such as students and teachers in schools. In addition, dynamic security groups can be customized based on 5W1H conditions.
Static security group (network resources)
Terminals or network segments that use fixed IP addresses, such as servers and the Internet.
  Static security groups are defined based on service types provided by network resources. For example, the school web server, the data server for storing student information, and the exam resource server can be divided into different static security groups.
The most important rule for defining a dynamic security group is to add users with the same network access requirements to one security group.
Who: identity of a user, for example, a corporate executive, employee, or guest;
Where: user access location, for example, local (within a campus) or remote access;
What: type of the access terminal, for example, a mobile phone, PC, or laptop;
When: time range when a user accesses the network, for example, in the daytime or at night;
Whose: device owner, for example, a company-issued terminal or BYOD terminal;
How: user access mode, for example, wired or wireless access.

## Slide 28: Permission Control Design
Define dynamic and static security groups for free mobility based on service requirements, and create a policy control matrix based on the required network access rights.
Dynamic security group
Hospital administrator
Doctor
Nurse
Patient
Static security group
Ward-round system server
Medical system server
Case database server
Internet
 | Ward-round system | Healthcare system | Case database | Internet | Hospital administrator | Doctor | Nurse | Patient
Hospital administrator | Permit | Permit | Permit | Permit |  | Permit | Permit | Deny
Doctor | Permit | Permit | Permit | Deny | Permit |  | Permit | Deny
Nurse | Deny | Permit | Deny | Deny | Permit | Permit |  | Deny
Patient | Deny | Deny | Deny | Permit | Deny | Deny | Deny | 
In addition to the overall policy control matrix, the administrator can further control user permissions based on applications. For example, allow patients to access the Internet, but disallow them to use applications such as shopping apps.
Source
Destination
Policy control matrix:
Notes: A security group policy reflects whether two security groups can communicate with each other. The administrator can configure policies to permit or deny communication between every two security groups in a policy control matrix on iMaster NCE-Campus. If no control policy is created for a source group and a destination group, they can communicate with each other by default.
When planning security group policies, pay attention to the direction of policies. Generally, packets are transmitted in both directions between two terminals.
  For Huawei switches, traffic from switch A to switch B and traffic from switch B to switch A match different policies. Whether traffic is permitted or denied depends on the source and destination groups of the traffic. If the permit action is configured for the A-to-B traffic and the deny action for the B-to-A traffic, all packets sent from switch A to switch B are allowed to pass through, but the packets sent from switch B to switch A are discarded, regardless of which device initiates the request. If no matching policy is found, a switch performs the default action — permit.
Generally, network access involves bidirectional communication. Therefore, to simplify management, you only need to consider the access permissions from user security groups to other users and servers when designing permission control policies.
  To prevent users from accessing a security group, you only need to configure a unidirectional deny rule.
  To allow users to access a security group, you only need to configure a unidirectional permit rule.

## Slide 29: User Authentication Design
The free mobility solution involves the same user authentication process as the traditional solution.
After a user is successfully authenticated, authorization information such as ACLs and VLANs is delivered in the traditional solution, whereas security group (UCL group) information is delivered in the free mobility solution.
Authentication modes supported by free mobility
Recommended locations of authentication points
Authentication Mode |  | Recommended Authentication Scenario
802.1X authentication |  | Wired user authentication
Portal authentication | Portal authentication | Wireless user authentication
 | MAC address-prioritized Portal authentication | 
MAC address authentication |  | Authentication for dumb terminals (such as printers)
PPPoE authentication |  | Authentication for education campus users
Device Role | Location
User authentication point | Core switch
 | Aggregation switch

## Slide 30: Locations of Authentication Points and Policy Enforcement Points
Typically, a user gateway functions as both the authentication point and policy enforcement point for the following major reasons:
  There are a large number of access switches on a network. Configuring the authentication function on each access switch requires a heavy workload and leads to difficulties in management.
  iMaster NCE-Campus needs to synchronize permission control policies to policy enforcement points. If access switches act as both authentication points and policy enforcement points, there will be a great number of policy enforcement points. This increases the workload and difficulties of device management on iMaster NCE-Campus and prolongs the policy synchronization time.
To prevent users on a Layer 2 network connected to an upstream user gateway from communicating with each other, configure Layer 2 isolation. In this way, communication traffic of the users must pass through the user gateway.
Notes: If the authentication point and policy enforcement point are located on different devices, the IP-security group entries of authenticated users need to be pushed to the specified policy enforcement point. An administrator can configure subscription on iMaster NCE-Campus to specify the entries of which network segments or security groups to be pushed to which policy enforcement points.

## Slide 31: Typical Free Mobility Solution
Core switch
(user gateway)
Access switch
Authentication point
Policy enforcement point
Intranet server
Internet
(Recommended) Core switch functioning as the user gateway, authentication point, and policy enforcement point
The core switch is used as the Layer 3 gateway and authentication point for wired and wireless users, as well as the policy enforcement point in the free mobility solution.
As the policy enforcement point is deployed at the upper layer, configure port isolation on access and aggregation switches to prevent traffic from being directly transmitted through the access or aggregation switches without passing through the core switch.
The policy enforcement points control mutual access between users and access from users to network resources such as servers, and are deployed on core switches.
When 802.1X authentication is used, configure transparent transmission of 802.1X packets on the access and aggregation switches if the authentication point is located on a core switch.
Aggregation switch

## Slide 32
(True or false) In the free mobility solution, a policy enforcement point must be an authentication point and is typically deployed on a user gateway. ( )
  True
  False
(True or false) Free mobility implements policy management and permission control based on security groups. Rules such as VLANs and ACLs need to be planned during network design. ( )
  True
  False
Notes: B
B

## Slide 33
Free mobility transforms IP-based policies into security group–based policies, which are easier to understand and decouple policies from IP addresses. This allows network administrators to implement policy control between security groups without considering the IP addresses of users.
Network objects of the same type and with the same permissions are added to one security group. Members in a security group can be PCs, mobile phones, printers, and servers. After network objects are divided into different security groups, administrators can define security group policies to determine the network services that each security group can use, including access rights and application control.