## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2021.02.15
Zhu Shigeng/00261992
Update
Lu Yueyue/WX445705
2021.08.15
Zhu Shigeng/00261992 & Liu Wei/00372307
Update

## Slide 2: Large- and Medium-Sized Virtualized Campus Network Design

## Slide 3
Huawei CloudCampus 3.0 Solution (hereafter referred to as Huawei CloudCampus Solution) adopts a new philosophy of Intent-Driven Network (IDN), and introduces big data analytics and Artificial Intelligence (AI) technologies into cloud and software-defined networking (SDN). It helps enterprises build intelligent, simplified, converged, open, and secure networks.
This course describes the planning and design process for large- and medium-sized virtualized campus networks that use the CloudCampus Solution, including the network architecture design, underlay network design, fabric and overlay network design, admission control and free mobility design, WLAN design, egress network design, network security and QoS design, as well as O&M design.

## Slide 4
On completion of this course, you will be able to:
  Describe the network layers and network architecture of large- and medium-sized virtualized campus networks.
  Complete the network architecture design and underlay network design for a virtualized campus network based on actual requirements.
  Complete the fabric and overlay network design for a virtualized campus network based on actual requirements.
  Complete the admission control design, free mobility design, WLAN design, egress network design, network security and QoS design, and O&M design for a virtualized campus network based on actual requirements.

## Slide 5
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 6: Large- and Medium-Sized Campus Networks
Different from the wide area network (WAN) and data center network, a campus network typically refers to the internal network of an enterprise or organization. A campus network is built for more efficient running of key enterprise services.
In terms of network scale, campus networks can be classified into large- and medium-sized campus networks as well as small- and medium-sized campus networks. A large- or medium-sized campus network typically has:
  Over 2,000 end users
  Over 100 network elements (NEs)
Some enterprises have branches dispersed across different areas, and each branch network can be considered a single campus network.

## Slide 7: Service Requirements and Challenges of Large- and Medium-Sized Campus Networks
Enterprises' campus networks are the cornerstone of their digital transformation. Nowadays, mobile office, cloud computing, SDN, Internet of Things (IoT), artificial intelligence (AI), and big data are gaining momentum. Driven by this, new technologies and applications are constantly emerging and are making inroads to enterprise campus networks, which poses many new challenges for the campus networks.
Converged network
Requirements:
Diversified access terminals and services require a converged campus network.
Challenges:
Wi-Fi and IoT services are independently planned, deployed, and managed, resulting in high network construction costs.
The network management and O&M workload is heavy.
User experience awareness
Requirements:
Network O&M should become automated and intelligent, with insights into user experience anytime, anywhere.
Challenges:
Service faults cannot be detected in a timely manner.
Fault locating heavily relies on the O&M skills and experience of professionals, so faults cannot be quickly located.
The network cannot be self-optimized.
Automated network deployment
Requirements:
Network deployment should be automated to address the growing complexity in deployment and policies due to the surge in applications and services.
Challenges:
Manual configuration is repetitive, complex, and labor-intensive.
New service rollout requires configuring devices one by one, which is time-consuming and costly.
The workload of network policy deployment and adjustment is heavy.

## Slide 8: Huawei CloudCampus 3.0 Solution (CloudCampus Solution)
Analysis
Management
Control
Design
Deployment
Policy
One-stop management platform
NETCONF/YANG
WAN/
Internet
Large- and medium-sized campus
Small- and medium-sized campus
Campus interconnection
OA VN
R&D VN
OA VN
R&D VN
Security group 1
Access policy
Bandwidth
Priority
Rapid network provisioning, improving deployment efficiency
Device plug-and-play: simplified device deployment, scenario-specific guided configuration, template-based configuration
Simplified network deployment: network resource pooling, multi-purpose network, automatic service provisioning
Fast service provisioning, improving user experience
Free mobility: GUI-based policy configuration; access anytime anywhere, with consistent permission and experience during roaming
Intelligent terminal identification: anti-spoofing for terminal access, with the accuracy of intelligent terminal identification reaching over 95%
Intelligent HQoS: application-based traffic scheduling and shaping and fine-grained bandwidth management ensure service experience of VIP users
Quick intelligent O&M, improving network performance
Real-time experience visualization: uses Telemetry for network experience visualization at any moment, for any user, and in any area
Precise fault analysis: proactively identifies typical network issues and provides suggestions; compares and analyzes real-time data to predict faults
Intelligent network optimization: predictive optimization of wireless networks based on historical data, improving overall network performance
Security group 2
Security group 3
Security group 4
Security group 5

## Slide 9: CloudCampus Highlights: Simplified Deployment
Physical and virtual network automation
Automated deployment of a physical network: Devices can be pre-configured for plug-and-play.
iMaster NCE-Campus provides a GUI for automated deployment of devices, as well as route orchestration and interworking configuration of underlay networks.
Automated provisioning of virtual networks: Virtual networks can be automatically created to achieve "one network for multiple purposes".
With iMaster NCE-Campus, fabric networks can be deployed, and VXLAN tunnels can be automatically set up based on the BGP EVPN control plane, so as to achieve automated virtual network construction, centralized service configuration, and automatic service provisioning.
Underlay (physical network layer)
OSPF
Overlay (virtual network layer)
VXLAN
VXLAN
User policy automation
Centering on users, services, and experience, policies can migrate with users, ensuring a consistent service experience.
The free mobility solution uses iMaster NCE-Campus to plan security groups and inter-group policies and automatically deliver policies to network devices.
When an authenticated user accesses the network using different terminals at different locations, iMaster NCE-Campus automatically identifies the user and delivers relevant user policies to the corresponding policy enforcement device on the network. This achieves consistent and assured user access experience. A user can have consistent policies and service experience, irrespective of the access location.
User A
User A
Move

## Slide 10: CloudCampus Highlights: Wired and Wireless Convergence
Huawei campus switches integrate the WLAN access controller (AC) functionality to implement wired and wireless convergence, providing unified management and experience for wired and wireless users.
NM Area
Native AC
CAPWAP
Unified forwarding
Wired and wireless traffic is centrally processed by the core switch before being forwarded.
Unified authentication
The core switch functions as the unified authentication point and Layer 3 gateway for both wired and wireless users.
Unified policy execution
The core switch is the policy enforcement point for both wired and wireless users.
Notes: By integrating the user authentication, user management, and policy association functions, the CloudCampus Solution provides unified authentication and access policy control for both wired and wireless users. Administrators can have a consistent user management experience, with simplified O&M for wired and wireless networks.

## Slide 11: CloudCampus Highlights: WLAN and IoT Convergence
Huawei APs integrate IoT modules to provide functions of IoT base stations, implementing Wi-Fi and IoT convergence as well as simplified management.
Internet
IoT AP
Store
IoT service management platform
Wi-Fi
Tag
Wi-Fi
Terminal
Bluetooth
Tag
RFID
Tag
IoT
Sensor
Wristband
Bluetooth
RFID
ZigBee
Scenarios and challenges
Scenarios: retail, healthcare, education, enterprise, and other campuses where innovative digital services need to be provided based on IoT.
Challenges: Wi-Fi and IoT (such as Bluetooth and RFID) networks are deployed separately. Numerous wireless networks are deployed, resulting in high costs and inflexible service expansion. There is also radio interference between these wireless networks, affecting service experience.
Huawei IoT AP
Wi-Fi & IoT converged architecture.
Converged site for the AP and IoT base station, reducing auxiliary resources (such as access and power supply management) by 50%.
Cloud-based management and plug-and-play, facilitating service configuration.
Wi-Fi and IoT configuration association, allowing automatic Wi-Fi channel switching when a conflict is detected.
ESL management
Healthcare IoT
Health management
Asset management
2.4 GHz (Wi-Fi)
Channel-6
2.4 GHz (RFID)
Channel-11

## Slide 12: CloudCampus Highlights: LAN and WAN Convergence (1)
MPLS
CPE1
Internet
CPE2
CPE3
HQ
Multi-service campus
Branch 1
Simple-service campus
Branch 2
Simple-service campus
SD-WAN
LAN management
Site management
Campus VXLAN
Free mobility
Site configuration
Access authentication
Resource management
WAN VPN
Route management
Intelligent traffic steering
One-stop management
Integrated GUI, improving deployment and O&M efficiency
Integrated deployment, integrated policy, integrated O&M
Diverse SD-WAN policies, improving application experience
Identification of 6000+ applications, application-based intelligent traffic steering, application-specific fine-grained QoS scheduling
One platform, reducing user investment
iMaster NCE-Campus can be deployed in a single-node system or a cluster.
Notes: CPE: Customer Premises Equipment
GUI: Graphical User Interface

## Slide 13: CloudCampus Highlights: LAN and WAN Convergence (2)
LAN-WAN interconnection solution
The CloudCampus Solution provides two technologies for campus egress interconnection: IPsec VPN and SD-WAN EVPN.
IPsec VPN is a static VPN technology that creates a VPN tunnel by setting up an IPsec tunnel between sites. It diverts traffic to a VPN tunnel based on the configured static network segments so that the sites can access each other through the VPN tunnel.
SD-WAN EVPN is a dynamic VPN technology that establishes tunnels between sites on demand and dynamically advertises routes. EVPN creates VPN tunnels between sites by setting up GRE tunnels between them. It supports IPsec encryption on the GRE tunnels, securing data transmission.
Application experience optimization policies provided on the WAN side:
Application identification, intelligent traffic steering, QoS, NAT policy, application optimization, etc.
Notes: Application identification:
  Precise identification of applications on a network is the prerequisite and basis for network services such as intelligent traffic steering, QoS, application optimization, and security. Service policies can be applied in subsequent service processes only after applications are identified.
  Two application identification methods are available in the SD-WAN EVPN Interconnection Solution: first packet inspection (FPI) and service awareness (SA).
Intelligent traffic steering:
  The SD-WAN EVPN Interconnection Solution supports traffic steering based on the application quality, load balancing, application priority, and bandwidth.

## Slide 14
Notes: QoS:
  QoS is a mainstream function that implements differentiated services. With this function, data packets are classified into different priorities or multiple class of services (CoSs) through traffic classification. These priorities and CoSs are the prerequisite and basis for the differentiated service (DiffServ) model. Different traffic policies can be configured based on packet priorities and CoSs to provide different services.
  The SD-WAN EVPN Interconnection Solution supports traffic classification based on the IP 5-tuple, application group, and DSCP, and supports QoS policies such as queue priority-based scheduling, traffic policing, and traffic shaping. It also supports QoS functions such as multi-dimensional bandwidth allocation and DSCP re-marking through HQoS.
NAT policy:
  Network Address Translation (NAT) translates the IP address in an IP packet header into another IP address.
  Huawei SD-WAN EVPN Interconnection Solution supports two types of NAT policies: dynamic NAT and static NAT.
Application optimization:
  Huawei SD-WAN EVPN Interconnection Solution uses the forward error correction (FEC) technology to mitigate audio and video packet loss. FEC uses a proxy to obtain data flows with specified 5-tuple information, adds verification information to packets, and verifies the packets at the receive end. If a packet is lost or damaged on the network, the verification information can be used to recover it.

## Slide 15: Three Deployment Modes of CloudCampus
Operations entity
Customer
MSP, carrier
Huawei
On-Premise
MSP-owned Cloud
Scenario definition
Target customer
Huawei Public Cloud
Customers purchase and own software entities, such as the controller and analyzer, which can be deployed in their data centers or on the public cloud platform.
MSPs purchase software, such as the controller and analyzer, for operational purposes. The software can be deployed in their data centers or on the public cloud platform.
Huawei operates the public cloud and customers do not need to purchase the controller or analyzer software. Instead, customers just purchase Huawei's cloud managed network service.
Customers in industries such as government, education, large enterprise, retail, and financial services
MSP, carrier
Customers in industries such as government, education, large enterprise, retail, and financial services
Software transaction mode
Perpetual license + SnS
TBL subscription mode
SaaS mode
Notes: Managed service provider (MSP): delivers and manages network-based services, applications, and devices. The serviced objects include enterprises, residential areas, and other service providers.
Perpetual license + SnS: The perpetual license is sold together with SnS services, such as software patches, software upgrades (including new features of new releases), and remote support. In the perpetual license + SnS mode, a customer needs to pay SnS fee for a certain period of time, in addition to purchasing the license upon the first purchase. If the customer does not renew the SnS annual fee after it expires, the customer can only use functions provided in the license for the current version and cannot use the service functions covered in the SnS annual fee.
SaaS mode: MSPs are responsible for deploying or leasing hardware infrastructure, and O&M and management of the hardware and software. Software is provided for customers as cloud services and customers need to periodically pay for the cloud services.
Term Based License (TBL) mode: This mode differs from the perpetual license + SnS mode in that the licenses purchased by customers have limited validity periods. If a customer does not renew the subscription after the license expires, the customer can no longer use the software product.
SnS: refers to Subscription and Support. It consists of two parts: software support and software subscription. The complete software charging mode consists of the annual software SnS fee and software license fee.
Note: This course uses the on-premise deployment as an example.

## Slide 16: CloudCampus Solution Components: iMaster NCE-Campus
iMaster NCE-Campus is the configuration and management platform used in the CloudCampus Solution. It provides a portal for CloudCampus service configuration, O&M, and monitoring.
Manage + Control + Analyze
Unified data base
Centralized detection/locating/processing
Plan + Construct + Maintain + Optimize
Full lifecycle management
Simulation/Verification/Monitoring/Optimization
iMaster NCE-Campus, an autonomous driving campus network management and control system
Application service layer
Infrastructure layer
Management-control-analysis layer
MDM
e-Schoolbag
Asset management
Health management
...
Intelligent OAM
Automated + Intelligent
SDN-based automatic service configuration/deployment
AI-powered intelligent analysis/prediction/troubleshooting
Converged

## Slide 17: CloudCampus Solution Components: iMaster NCE-CampusInsight
AS-IS: Device-centric network management
TO-BE: User experience-centric AI-powered intelligent O&M
Device-centric management: User experience cannot be perceived.
Passive response: Potential faults cannot be identified.
Professional engineers locate faults on site.
SNMP
Network data collection within minutes
Topology management
Performance management
Alarm management
Configuration management
Experience visibility: Telemetry-based second-level data collection, enabling visible experience for each client, in each application, and at each moment.
Identification of potential faults and location of root causes within minutes:
  Identification of potential faults based on dynamic baselines and big data correlation analysis.
  KPI correlation analysis and protocol trace, helping accurately locate root causes of faults.
Predictive network optimization: intelligently analyzes load trends of APs through AI algorithms, implementing predictive optimization of wireless networks.
Traditional NMS
Telemetry
Network data collection within seconds
Visualized experience management
User journey playback
Identification of potential faults
Location of root causes
Predictive network optimization
Notes: Using algorithms to improve efficiency and leveraging scenario-specific continuous learning and expert experience, intelligent O&M frees O&M personnel from nerve-wracking alarms and noises, making O&M automated and intelligent.

## Slide 18: CloudCampus Solution Components: WLAN Planner
WLAN Planner is an efficient WLAN network planning tool. It simulates signals to determine APs' deployment positions and signal coverage.
Notes: Efficiently supports WLAN network planning:
  No installation: Cloud-based tool, without the need of software installation.
  All-scenario: All scenarios supported, including indoor, outdoor, agile distributed, and high-density scenarios.
  Efficient: Improved simulation efficiency when compared with the traditional standalone deployment.
  High quality: Supports tens of thousands of WLAN projects.
For more information about the WLAN, such as WLAN planning, SSID planning, and radio calibration, see the Small- and Medium-Sized Cloud-Managed Campus Network Design or HCIX-WLAN series courses.

## Slide 19: CloudCampus Solution Components: Network Hardware Products
CloudEngine S series switches
AirEngine Wi-Fi 6 APs
High-performance campus switches
Campus APs
Models that apply to all scenarios: indoor settled, indoor wall plate, agile distributed, and outdoor AP models
NetEngine AR routers
Campus egress routers
Integrate routing, switching, Wi-Fi, 5G, and security functions
HiSecEngine AI firewalls
Firewalls
Provide comprehensive and integrated network security protection capabilities

## Slide 20: Network Architecture of the CloudCampus Solution (VXLAN-based Virtualized Campus Network)
The following figure shows the typical network architecture of the CloudCampus Solution, which consists of the network layer, management layer, and application layer.
Application layer
Network layer
Management layer
MDM
e-Schoolbag
Asset management
Health management
AAA
…
Intelligent OAM
VN 1
VN 3
VN 2
Virtual network
Internet/
WAN
Native AC
AP
Switch
Switch
Switch
Switch
Switch
Firewall
Physical network
Open APIs
SNMP
NETCONF/
YANG
Telemetry
Notes: Network layer
  Virtualization technologies are introduced to divide the network layer into a physical network and a virtual network.
    Physical network: is also called the underlay network and provides basic connection services for a campus network. To meet access requirements of multiple types of terminals, the physical network provides converged access for three networks, allowing simultaneous access of wired, wireless, and IoT terminals.
    Virtual network: is also called the overlay network. Virtualization technology is used to construct one or more overlay networks on top of the underlay network. Service policies are deployed on the overlay networks and are separated from the underlay network, decoupling services from networks. Multiple overlay networks can serve different services or customer segments.

## Slide 21
Notes: Management layer
  The management layer provides management capabilities, such as configuration management, service management, maintenance and fault detection, as well as security threat analysis. Traditional campus networks use a network management system (NMS) for network management. Although the NMS can display the network status, it lacks flexibility and automatic management capability. Once service requirements change, the network administrator needs to re-plan services and manually modify configurations on network devices (including routers, switches, and firewalls), which is inefficient and error-prone. Therefore, maintaining network flexibility is critical in rapidly changing service environments, which requires the use of automation tools to assist in network and service management. Huawei's CloudCampus Solution uses iMaster NCE-Campus to implement automatic network and service provisioning.
  iMaster NCE-Campus abstracts network devices and applications, and rapidly develops and automatically deploys applications through orchestration and by invoking abstract models. iMaster NCE-Campus illustrates the entire network but not independent devices (such as switches, routers, and APs) or discrete configurations (such as access control, QoS, and routing policies) on devices.
Application layer
  Based on iMaster NCE-Campus, Huawei CloudCampus Solution provides open standards-compliant APIs, through which various information including user identities, network resources, service quality, location information, and network topology, is opened up to upper-layer services. Third parties can use these APIs to customize innovative service applications based on service demands, meeting service requirements in multiple fields such as education, commerce, enterprise, and government.

## Slide 22: Architecture of a Virtualized Campus Network
Underlay (physical network layer)
Fabric
Core
Aggregation
Aggregation
Access
Access
Border
BGP EVPN
BGP EVPN
External network
Network service resources
Edge
Edge
Wired access
Wireless access
Overlay (virtual network layer)
VN 1
VN N
VRF+VNI
VRF+VNI
Network egress
IP/VLAN
Access point
Network services
Fabric instantiation
OSPF
VXLAN
Underlay: a physical topology consisting of physical network devices (such as switches, APs, firewalls, and routers) that provide interconnection capabilities for all services on the campus network. It is the basic bearer network for campus service data forwarding.
Fabric: a network with pooled resources abstracted from the underlay network. When creating an instantiated VN, you can select network resources on the fabric.
Virtual network (VN): a logically isolated virtual network instance that is constructed by instantiating a fabric. One VN corresponds to one isolated network (service network), for example, R&D network.
Notes: On a large- or medium-sized campus network, the virtualization solution may need to be used to decouple services from the network, so as to build a multi-purpose network and achieve flexible, fast service deployment without changing the basic network infrastructure. Using such a solution means that the virtualized campus network architecture must be different from the traditional network architecture.
This slide presents the virtualized campus network architecture. The underlay is the physical network layer, and the overlay is the virtual network layer constructed on top of the underlay using the Virtual Extensible LAN (VXLAN) technology.

## Slide 23: Network Nodes on a Virtualized Campus Network
Egress gateway: is an egress device of the campus network, which can be an AR router or a firewall.
Firewall node: This node is required when Layer 4 to Layer 7 security policies are deployed. It can be deployed in off-path mode or at the campus egress.
Border node: implements communication between the fabric and external networks. It is typically a core switch.
Transparent node: It does not need to support VXLAN.
Edge node: is a fabric edge device that connects user-side devices to the fabric. Data packets from wired users enter the VXLAN network through edge nodes.
Access node: is typically an access switch (wired access node) or an AP (wireless access node). Wired access nodes can function as edge nodes, that is, VXLAN is deployed across core and access nodes. If wired access nodes do not need to support VXLAN, aggregation nodes can function as edge nodes — that is, VXLAN is deployed across core and aggregation nodes — in which scenario policy association can be deployed on wired access nodes and edge nodes.
Fabric domain (VXLAN)
Access domain
Border node
Transparent node
Edge node
Access node
VXLAN-capable nodes
Egress gateway
Firewall node
Notes: On a fabric network, a VXLAN tunnel endpoint (VTEP) can function as either a border or edge node:
  Border node: It corresponds to a physical network device and forwards data between the fabric and external networks. In most cases, border nodes are VXLAN-capable core switches.
  Edge node: It corresponds to a physical network device. User traffic enters the fabric from the edge node. Typically, edge nodes are VXLAN-capable access or aggregation switches.
Policy association:
  Policy association provides a solution to contradiction between policy strengths and complexity on large campus networks. In the solution, user access policies are centrally managed on the gateway devices and enforced by gateway and authentication access devices.
  After policy association is configured, authentication access devices can transparently transmit BPDUs and report user logout and user access positions in real time. In addition, the authentication control device requests authentication access devices to enforce user access policies, thus controlling user access to the network.

## Slide 24: Key Technologies in CloudCampus: DHCP-based Plug-and-Play of Network Devices
The network administrator has deployed the DHCP service on the network. (It is recommended that the DHCP service be deployed on the core switch.)
In addition to delivering an IP address to the device to be deployed, the DHCP server uses DHCP Option 148 to notify the device of the iMaster NCE-Campus IP address and port number.
Core switch
1
2
DHCP request
3
DHCP response: includes the IP address, DNS, working mode, and Option 148 (containing the iMaster NCE-Campus IP address and port number)
4
The switch proactively initiates a registration request to iMaster NCE-Campus.
Devices supported: AR routers, switches, APs
Switch to be deployed

## Slide 25: Key Technologies for Virtualized Campus: Admission Authentication
Authentication point
VXLAN
Border
Core
Aggregation
Access
Egress
AP
Edge
Edge
Built-in server of iMaster NCE-Campus
RADIUS server & Portal server
Sales
(802.1X)
Guest
(Portal)
Request for user identity authentication
Transfer of user identity credential
User identity verification
User policy authorization
1
2
3
4
Phone
(MAC)
Service traffic
Notes: Request for user identity authentication: The terminal sends its identity credential to the admission device.
User identity authentication: The admission device sends the identity credential to the admission server for identity authentication.
User identity verification: The admission server stores user identity information and manages users. After receiving the identity credential of the terminal, the admission server verifies the identity of the terminal, determines whether the terminal identity is valid, and delivers the verification result and policy to the admission device.
User policy authorization: As a policy enforcement device, the admission device implements policy control over the terminal based on the authorization result provided by the admission server, for example, permitting or denying network access, or performing more complex policy control on the terminal. Complex policy control can be increasing or decreasing the forwarding priority of the terminal, or restricting the network access rate of the terminal.

## Slide 26: Key Technologies for Virtualized Campus: Policy Association
If access switches do not support VXLAN, policy association can be deployed between access and aggregation switches (gateways). The gateway manages user access policies in a unified manner, and the access switch enforces user access policies.
  Authentication control points and enforcement points are connected through CAPWAP tunnels (which are the management tunnels used by policy association).
  CAPWAP tunnels implement user association, message transmission, user authorization policy delivery, user information synchronization, and other functions.
  After policy association is configured, authentication enforcement points can transparently transmit BPDUs, report user logout and access locations in real time, and enforce user access policies, thereby controlling user access to the network.
CSS/iStack
Authentication control point
Authentication enforcement point
CAPWAP tunnel
VXLAN
Border
Edge
Edge
Edge
L2
L3
Access
AP
Access
Policy association
Policy association
Link aggregation
Core
Aggregation
Access
Egress
Notes: CAPWAP: Control and Provisioning of Wireless Access Points

## Slide 27: Key Technologies for Virtualized Campus: Free Mobility
Free mobility manages policies and controls permissions based on security groups. Regardless of user locations and IP addresses in use, this technology ensures that users can obtain consistent network permissions and corresponding policies can be enforced on the users.
Campus network
User A
User B
User C
Admission authentication
Admission authentication
Admission authentication
Security group and policy delivery
3
4
2
Sales user
security group
R&D user
security group
Server
resource group
Permission control policies
1
Create security groups. A security group is a group of users or network resources that have the same network access policies.
Define permission control policies based on security groups and deliver the policies to network devices.
Authorized security groups are assigned to the users who pass admission authentication.
After user traffic enters the network, network devices enforce policies based on the corresponding source and destination security groups of the traffic.
Notes: Free mobility introduces the concept of security group. Security groups are related only to user identities and are completely decoupled from network information such as user VLANs and IP addresses.
User policy management and permission control are performed based on security groups.

## Slide 28: Key Technologies in CloudCampus: Terminal Identification
Difficult to locate bogus terminals.
Example: an enterprise
10+ authentication faults reported per day
50+ types of smart terminals
Example: higher education institution
Data of smart terminals collected by level-2 departments.
Difficult and error-prone MAC address collection.
Terminal type-based
Automatic authorization
Recognized as a camera
Automatically added to a video surveillance group.
Terminal type-based
Automatic authentication
Recognized as a printer
Automatic MAC address authentication, without the need of manual MAC address input.
Terminal type-based
Bogus terminal detection
Recognized as an IP phone first and then a PC
Report a bogus terminal alarm.
Requirements and challenges
Terminal identification and policy automation
Terminal fingerprint database
Information reporting
Proactive scanning
>>
Notes: On large- and medium-sized campus networks, access terminals include smart terminals (such as PCs and mobile phones) and dumb terminals (such as IP phones, printers, and IP cameras). Currently, terminal management on campus networks faces the following challenges:
  The network management system (NMS) can only display the IP and MAC addresses of access terminals, but cannot identify the specific terminal type. As a result, the NMS cannot provide refined management for network terminals.
  Network service configurations and policies vary according to the terminal type. Consequently, administrators need to manually configure different services and policies for each type of service terminals, complicating service deployment and operations.
To address these challenges, Huawei provides the automatic terminal identification and policy delivery solution, which delivers the following functions:
  iMaster NCE-Campus can display the network-wide terminal types and operating systems, for example, dumb terminals including printers, IP cameras, smart all-in-one card, and access control system. iMaster NCE-Campus can also collect statistics and display traffic by terminal type.
  Administrators do not need to manually configure different services and policies for different types of dumb terminals such as IP phones, printers, and IP cameras on the campus network. Instead, iMaster NCE-Campus can automatically identify these terminals and deliver the corresponding admission policies and service configurations to them.

## Slide 29: Terminal Identification Modes
Passive fingerprint-based identification
Proactive scanning and identification
Terminal visibility: collects terminal type statistics (by vendor and OS), displays the relationship between terminals and access ports, queries access policies (VLAN, QoS, and authentication mode), and exports reports.
Terminal policy automation:
  Supports automatic terminal access based on terminal types, thereby achieving automatic MAC address authentication of dumb terminals.
  Authorizes policies (covering VLAN, security group, access permission, and QoS) on a per-terminal group basis; supports IPv4/IPv6 dual-stack terminals.
Scan-and-detect
Information reporting
1
2
4
3
Identification result display
Administrator
6
Policy delivery
5
Identification result display
Administrator
1
Traffic sent from the terminal
Fingerprint collection
2
3
Fingerprint reporting
4
Fingerprint matching against the fingerprint database
Policy delivery
Notes: Passive fingerprint-based identification: Network devices collect fingerprints of packets sent by terminals and report the fingerprints to iMaster NCE-Campus, which matches the fingerprints against its fingerprint database for terminal type identification. In this mode, terminals can be identified through a MAC organizationally unique identifier (OUI), HTTP User-Agent, DHCP Option, LLDP, and multicast DNS (mDNS).
Proactive scanning and identification: iMaster NCE-Campus proactively detects or scans terminals, and identifies terminal types based on fingerprint information of the terminals. In this mode, terminals can be identified through SNMP query or network mapper (Nmap).

## Slide 30: Terminal Identification Methods
The terminal management function of iMaster NCE-Campus can help identify terminals and display the terminal type, operating system, and manufacturer.
The following table describes terminal identification methods.
Type | Identification Method | Method Description | Application Scenario
Passive fingerprint-based identification (information reporting) | MAC OUI | The first three bytes of a MAC address represent the manufacturer. | Identifies the device manufacturer only.
 | HTTP User-Agent | A browser's User-Agent string contains the manufacturer, terminal type, operating system, browser type, and other information. | Mobile phones, tablets, PCs, workstations, smart audio and video terminals.
 | DHCP Option | Some options of a terminal's DHCP packets can be used to classify terminals, for example, DHCP options 55, 60, and 12. | Mobile phones, tablets, PCs, workstations, IP cameras, IP phones, printers, etc.
 | LLDP | LLDPDUs carry device model information. | IP phones, IP cameras, network devices, etc.
 | mDNS | mDNS packets contain terminal model and service information. | Printers, IP cameras, etc.
Proactive scanning and identification | SNMP Query | Obtains identification information by querying device information-related SNMP MIB objects. | Network devices, printers, etc.
 | Nmap | Scans the OS and services of terminals to detect the terminal model and OS information. | PCs, workstations, printers, phones, IP cameras, etc.
Notes: When terminals access the network, network devices can collect terminal information and report the information to iMaster NCE-Campus. Alternatively, iMaster NCE-Campus can proactively scan terminals to identify the terminal type, OS, and manufacturer.

## Slide 31: Process of Automatic Policy Delivery Based on Terminal Types
On the iMaster NCE-Campus GUI, an administrator enables the terminal identification function, selects terminal types, and specifies the corresponding policies.
iMaster NCE-Campus delivers terminal identification configurations to network devices.
When terminals access the network, network devices collect the fingerprint information of the terminals and report the information to iMaster NCE-Campus.
iMaster NCE-Campus automatically matches the terminals' fingerprint information against the fingerprint database to identify the terminal types.
iMaster NCE-Campus automatically delivers admission and authorization policies to the terminals based on the policies defined by the administrator.
The administrator enables terminal identification and configures terminal policies.
The network device reports terminal fingerprint information.
iMaster NCE-Campus delivers configurations to network devices.
iMaster NCE-Campus matches the terminal's fingerprint information against the fingerprint database and identifies the terminal type.
iMaster NCE-Campus delivers admission and authorization policies for the terminal to the network device.
1
3
2
4
5

## Slide 32: Key Technologies for Virtualized Campus: VXLAN-based Multi-purpose Network
OA
VC
Security protection
Internet
OA
VC
Security protection
Internet
OA
VC
Security protection
VXLAN
VN1
OA VN
VN2
VC VN
VN3
Security protection VN
Multiple services carried on one physical network
Automated physical network deployment
Automated VN provisioning
Automated service policy delivery
Notes: Using virtualization technologies, multiple virtual networks (VNs) can be created on top of a physical network. Different VNs are used for different services, such as OA, videoconferencing, and security protection.
VC: Video Conference

## Slide 33: Overview of Large- and Medium-Sized Virtualized Campus Network Design
Network architecture design
Underlay
network design
Basic service design
LAN automation
design
Fabric design
Networking and node
design
External network
interconnection design
Network service
resource planning
Access management design
Overlay
network design
VN design
Policy design
VN access design
Admission control and
free mobility design
User management design
Admission control design
Free mobility design
Terminal identification design
WLAN design
Networking scheme
Egress network design
Egress networking design
Hot standby design
Egress routing design
Security zone design
Security policy design
Network security and
QoS design
Egress security
Intranet security
QoS design
O&M design
Infrastructure network
O&M design
Intelligent O&M design
Virtualized campus network design

## Slide 34
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 35: Network Architecture Design Overview
Overall design principles:
  Tree and ring(Core devices) network topologies
Reliability considerations:
  High reliability of nodes: CSS, iStack, and hot standby (AC, firewall, etc.)
  High reliability of links: redundant links and Eth-Trunk
Network layer design principles:
  Two-layer networking: The network layers are simple, and faults are easy to locate.
  Three-layer networking: applies to campuses with multiple buildings or regions.
iStack/CSS link
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
Internet
WAN
O&M zone
DC
Notes: Large- and medium-sized campus networks often use the tree topology with the core layer as the root, as shown in the figure. This topology is stable and easy to expand and maintain. A campus network can be divided into the following layers: access layer, aggregation layer, core layer, and multiple zones including the egress zone, DC zone, and O&M zone. Internal changes within a module have limited impact on other modules, facilitating fault location.
Terminal layer
  The terminal layer involves various types of terminals that access the campus network, such as PCs, printers, IP phones, mobile phones, and cameras.
Access layer
  The access layer provides various access modes for users and is the first network layer for terminals to access a campus network. The access layer is usually composed of access switches. There are a large number of access switches that are sparsely distributed in different places on the network. In most cases, an access switch is a simple Layer 2 switch. If the terminal layer has wireless terminals, the access layer provides APs that access the network through access switches.
Aggregation layer
  The aggregation layer connects the access layer to the core layer. The aggregation layer forwards horizontal traffic between users and forwards vertical traffic to the core layer. It can also function as the switching core for a department or zone and connect the department or zone to the exclusive server zone. In addition, the aggregation layer can further extend the quantity of access terminals.

## Slide 36
Notes: Core layer
  The core layer is the core for data exchange on a campus network. It connects various components of a campus network, such as the DC zone, aggregation layer, and egress zone. The core layer is responsible for high-speed interconnection of the entire campus network. High-performance core switches need to be deployed to implement high bandwidth utilization and fast convergence upon network faults. It is recommended that the core layer be deployed if a campus has more than three departments. For a wireless network, the core layer includes ACs. After a wireless terminal accesses the network through an AP, the AP communicates with an AC using a CAPWAP tunnel.
Egress zone
  The campus egress is the boundary between a campus network and an external network. Internal users of the campus network can access the external network through the campus egress zone, and external users can access the internal network through the campus egress zone. The campus egress zone typically has routers and firewalls deployed. The routers enable interconnection between internal and external networks, and the firewalls provide border security protection.
DC zone
  In the DC zone, service servers such as the file server and email server are managed, and services are provided for internal and external users.
O&M zone
  In the O&M zone, network servers such as the network management system and authentication server are managed. The standard NMS interacts with network devices through the Simple Network Management Protocol (SNMP) and provides configuration, management, and maintenance functions. For example, it provides network topology and port display management, network device configuration management, network fault diagnosis and alarm, as well as network performance and status analysis. Huawei CloudCampus Solution provides intelligent O&M based on NETCONF and telemetry.
In addition to these, a campus may have a demilitarized zone (DMZ). The DMZ contains public servers that can be accessed by guests (non-employees), therefore the access permission to this zone is strictly controlled.

## Slide 37: Network Architecture Design (1)
In actual applications, you can choose the three-layer or two-layer architecture based on the network scale or service requirements.
Block 1
Block N
Three-layer architecture
Two-layer architecture
Core layer
Aggregation layer
Access layer
Core layer
Access layer
Application scenario: large campus networks with a large number of users or involving multiple buildings (for example, campus networks of high education institutions)
Application scenario: small- and medium-sized campus networks involving only one building
Layered design
Modular design
Redundancy design
Symmetric design
Notes: Layered design:
  Each layer can be considered a well-structured module with specific roles and functions. This layered structure is easy to expand and maintain, reducing the design complexity and difficulty.
Modular design:
  Each module corresponds to a department, function, or service area. Modules can be expanded flexibly based on the network scale, and adjustment in a department or area does not affect other departments or areas, which facilitates fault locating.
Redundancy design:
  Dual-node redundancy design can ensure device-level reliability. Appropriate redundancy improves reliability, but excessive redundancy makes O&M difficult. If dual-node redundancy cannot be implemented, you may consider card-level redundancy, such as dual main control boards or switch fabric units (SFUs), for modular core switches or egress routers. In addition, Eth-Trunk can be deployed for important links to ensure link-level reliability.
Symmetric design:
  A symmetric network structure makes the topology clearer and facilitates service deployment, protocol design and analysis.

## Slide 38: Network Architecture Design (2)
During network design, you can use the bottom-up method to determine the type of architecture based on the network scale.
1. Determine the number of access ports
2. Select access switches
3. Calculate the number of access switches
4. Select aggregation switches
5. Calculate the number of uplinks of access switches
6. Calculate the number of aggregation switches
Three-layer architecture
Two-layer architecture
Single-layer architecture
If a single port corresponds to a single user or a specific number of users, you can determine the number of required access ports based on the network scale.
Determine the appropriate access switches (including access capability, port density, and uplink mode) based on the port rates of terminals' NICs.
Quantity = Number of access ports/Number of downlink ports on a switch
Select the appropriate aggregation switches based on the uplink port rates of access switches.
Quantity = Required network bandwidth/Uplink port rate of an access switch
Quantity = (Number of access ports x Access port rate x Bandwidth oversubscription ratio)/Uplink port rate of an access switch
Quantity = Number of uplinks of access switches/Number of downlink ports of an aggregation switch
N
Y
Y
N
Quantity > 1?
Quantity > 1?
Notes: Design method of the hierarchical model for common network architectures:
  Determine the number of access switch ports based on the network scale. Typically, one port corresponds to one terminal or one network access point (for example, AP).
  Select switches based on the port rates of terminals' NICs.
  Calculate the number of access switches.
    Number of access switches required = Number of access ports/Number of downlink ports on a switch
    If the calculation result is greater than 1, aggregation switches need to be deployed. Otherwise, use the single-layer architecture.
  Select aggregation switches based on the uplink port rates of access switches.
  Calculate the number of uplinks of access switches using either of the following methods:
    Based on the network bandwidth: Number of uplinks = Network bandwidth/Uplink port rate of an access switch
    Based on the network scale: Number of uplinks = (Number of access ports x Access port rate x Bandwidth oversubscription ratio)/Uplink port rate of an access switch

## Slide 39
Notes:   Calculate the number of aggregation switches.
    Number of aggregation switches required = Number of uplinks of access switches/Number of downlink ports of an aggregation switch
    If the result is greater than 1, select the three-layer architecture. Otherwise, use the two-layer architecture.
Notes:
  In the preceding calculations, the calculation results need to be rounded up.
  Bandwidth oversubscription ratio = Actual downlink bandwidth of a service/Maximum physical bandwidth provided by a single switch
    Traffic of the service may exhaust the maximum physical bandwidth. However, this probability is low in most cases. Generally, network planning focuses on service experience in common situations. That is, certain bandwidth redundancy is designed when actual possible bandwidth is met.
    Before designing a network traffic oversubscription ratio, we need to understand the service applications and features to be deployed on the network and determine the network services and traffic models. Additionally, the volume and ratio of traffic must be thoroughly considered before designing an oversubscription ratio and selecting devices.

## Slide 40
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 41: Underlay Network Design Outline
1. Basic service design
2. LAN automation design
VLAN planning
IP address planning
DHCP service design
Routing design
Network deployment design
Underlay network automation

## Slide 42: VLAN Design
You are advised to assign consecutive VLAN IDs to ensure proper use of VLAN resources.
You are advised to reserve a certain number of VLANs for future expansion.
VLANs are classified into service VLANs, management VLANs, and interconnection VLANs.
Typically, VLANs are assigned based on interfaces. According to different design principles, interfaces of access switches are added to different VLANs so that users of different service types can be isolated.
Service VLAN design
Management VLAN design
VLAN assignment based on geographical areas
VLAN assignment based on logical areas
VLAN assignment based on the personnel structure
VLAN assignment based on service types
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
In most cases, a Layer 2 switch uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches use the same management VLAN and their management IP addresses be on the same network segment.
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: Service VLAN:
  Assign VLANs by logical area, geographical area, personnel structure, or service type.
    Assign VLANs by logical area. For example, VLANs 100 to 199 are used in the core network zone, VLANs 200 to 999 are used in the server zone, and VLANs 2000 to 3499 are used on the access network.
    Assign VLANs by geographical area. For example, VLANs 2000 to 2199 are used in area A, and VLANs 2200 to 2399 are used in area B.
    Assign VLANs by personnel structure. For example, department A uses VLANs 2000 to 2009, and department B uses VLANs 2010 to 2019.
    Assign VLANs by service type. For example, VLANs 200 to 299 are used in the web server zone, VLANs 300 to 399 are used in the app server zone, and VLANs 400 to 499 are used in the database server zone.
  If users are sensitive to the voice latency, the voice service must be preferentially guaranteed. It is recommended that the voice VLAN be planned for the voice service. Huawei switches can automatically identify voice data, transmit voice data in the voice VLAN, and perform QoS guarantee. When network congestion occurs, voice data can be preferentially transmitted.

## Slide 43
Notes:   If different users have the same multicast data service, you are advised to plan a multicast VLAN and bind the user VLANs to the multicast VLAN. This prevents the upstream gateway from copying multicast data in multiple user VLANs.
  Do not use VLAN 1 as a service VLAN.
Management VLAN:
  It is recommended that the management VLAN be planned for a Layer 2 switch and the VLANIF interface of the management VLAN be used as the management interface, through which the NMS manages the switch. It is recommended that all Layer 2 switches use the same management VLAN.
  It is recommended that service interfaces be used as management interfaces of Layer 3 devices (gateways and their upstream devices), and no management VLAN needs to be planned for these devices.
Interconnection VLAN:
  An interconnection VLAN is usually configured between two Layer 3 switches or between a Layer 3 switch and a router. Create VLANIF interfaces for Layer 3 interconnection.

## Slide 44: IP Address Design
IP addresses of a campus network are classified into service, management, and interconnection IP addresses.
Management IP address
A Layer 2 device uses the VLANIF interface's IP address as the management IP address. It is recommended that all Layer 2 switches connected to a gateway be on the same network segment.
Management VLAN 100
VLANIF 100
192.168.100.1
VLANIF 100
192.168.100.2
VLANIF 100
192.168.100.254
Service and interconnection IP addresses
Service IP addresses are the IP addresses of servers, hosts, and gateways.
It is recommended that gateway IP addresses have the same last octet, for example, .254.
The IP address range of each service must be clearly differentiated. The IP addresses for each type of service terminals must be contiguous and can be aggregated.
You are advised to use IP address segments with a 24-bit mask.
It is recommended that the interconnection IP address use a 30-bit mask. The core device uses an IP address with a small host address.
Employee
192.168.40.0/24
Partner
192.168.50.0/24
Guest
192.168.100.0/24
VLANIF 200: 192.168.200.1/30
VLANIF 200: 192.168.200.2/30
Interconnection VLAN 200
Service VLAN 40/50/100
VLANIF 40: 192.168.40.254
VLANIF 50: 192.168.50.254
VLANIF 100: 192.168.100.254
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: IP address planning complies with the following principles:
  Unique: Each host on an IP network must have a unique IP address.
  Contiguous: Node addresses of the same service must be contiguous to facilitate route planning and summarization. Contiguous addresses facilitate route summarization, thereby reducing the size of the routing table and speeding up route calculation and convergence.
  Scalable: Some IP addresses need to be reserved at each layer, so that no address segments or routing entries need to be added when the network is expanded.
  Easy to maintain: Device and service address segments need to be clearly distinguished from each other, facilitating subsequent statistics monitoring and security protection based on address segments. IP addresses can be planned based on VLANs.

## Slide 45
Notes: Pay attention to the following points when designing the three types of IP addresses:
  Service IP address:
    Considering the scope of a broadcast domain and easy planning, it is recommended that an IP address segment with a 24-bit mask be reserved for each service. If the number of service terminals exceeds 200, another IP address segment with a 24-bit mask is reserved.
  Management IP address:
    It is recommended that a Layer 3 device use a Layer 3 interface for management and deployment. The interface address is used as the management IP address for local login and communication with iMaster NCE-Campus.
  Interconnection IP address:
    Interconnection addresses are usually aggregated before being advertised. Therefore, you need to use contiguous and aggregatable addresses during planning.
In addition, if devices at the aggregation and access layers are interconnected, you need to plan IP addresses for policy association in some cases. The IP addresses must be planned based on the entire CloudCampus network and cannot conflict with other service IP addresses.

## Slide 46: Terminal-Oriented DHCP Service Design
Plan an independent DHCP server to allocate IP addresses to terminals.
You are advised to configure DHCP snooping on access devices to defend against attacks.
Network administrators can use either of the two mechanisms to assign IP addresses to hosts based on network requirements:
  Dynamic IP address assignment: An IP address is assigned to a host with a lease. This mode applies to scenarios where hosts require temporary access or IP addresses are insufficient, for example, portable computers of traveling employees and mobile terminals in cafes.
  Static IP address assignment: Fixed IP addresses are assigned to specified hosts or servers such as DNS servers.
When planning an address pool, filter out static IP addresses.
The lease needs to be planned based on the online duration of a client.
On a large or midsize campus network, the DHCP server and hosts are usually not on the same network segment. Therefore, you need to enable the DHCP relay function on the gateway.
DHCP server
DHCP clients
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation

## Slide 47: Routing Design
Three-layer networking: scenario 1
Three-layer networking: scenario 2
OSPF area 0
OSPF area 1
OSPF area 2
Core (border)
Aggregation
Access (edge)
OSPF area 0
Core (border)
Aggregation
Access (edge)
Three-layer networking:
  Scenario 1 (multi-area): The interconnection links between core switches belong to OSPF area 0, and the links connecting the core switch to each aggregation switch belong to an independent OSPF area.
  Scenario 2 (single-area): Core, aggregation, and access switches all work in OSPF area 0. If the number of switches to be deployed in a network area is fewer than 100, scenario 2 is recommended.
  Two-layer networking:
  OSPF runs only between core switches and access switches. In this case, only OSPF area 0 needs to be planned on the entire network.
CSS/iStack link
CSS/iStack link
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: The routing design includes internal and egress routing design for a campus network.
  Internal routing design:
    The routing design must support communication between devices, between terminals, and between devices and terminals on the campus network, as well as communication between these devices/terminals and the external network.
    It is recommended that you design internal routes based on the gateway location.
      If gateways are deployed at the aggregation layer, routes need to be deployed at core and aggregation layers. Routing tables can be dynamically updated along with network topology changes, so an Interior Gateway Protocol (IGP), such as Open Shortest Path First (OSPF), is recommended.
      If gateways are deployed at the core layer, you only need to configure routes at the core layer. It is recommended that static routes be used preferentially.

## Slide 48
Notes:   Egress routing design:
    Egress routes must enable internal terminals to access the Internet and WAN.
    A large or medium-sized campus network usually has a large number of branches. The egress needs to support multiple links for Internet access and mutual communication between enterprise branches. For this purpose, a large number of routes need to be imported to the campus network. Therefore, you are advised to plan a dynamic routing protocol such as OSPF.
It is recommended that OSPF be planned for a campus network. The OSPF design precautions are as follows:
  You are advised to use the IP addresses of loopback interfaces as the router IDs.
  Areas are divided according to the core, aggregation, and access layers. It is recommended that egress routers and core switches be deployed in the backbone area. The design of non-backbone areas depends on the geographical location and performance of devices.
Note:
  This slide describes the routing design in the scenario when VXLAN is deployed across core and access layers.
  In the scenario where VXLAN is deployed across core and aggregation layers, the routing design (for example, OSPF area division) is the same as when VXLAN is deployed across core and access layers. The only difference is that the aggregation device is the border of the routing domain.

## Slide 49: Network Deployment Design
CSS/iStack link
Native AC
Core
Aggregation
Access
Traditional deployment
Plug-and-play
Traditional deployment (via CLI or web system):
Egress router
Egress firewall
Core switch
Standalone AC
Plug-and-play:
Aggregation switch
Access switch
AP
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: Typically, egress and core devices on large- and medium-sized campus networks are centrally deployed in a core equipment room. Services transmitted on these devices are complex and their locations on the network are important. In most cases, network engineers need to commission devices onsite during the deployment. Therefore, you are advised to use the web system or CLI to deploy devices at the core layer and upper layers (including core devices, standalone ACs connected in off-path mode, and egress devices).
A large number of devices (including aggregation devices, access devices, and APs) are deployed at lower layers of the core layer, and service configurations of these devices are similar. Therefore, you are advised to use the DHCP option mode to achieve plug-and-play of devices, thereby simplifying the deployment.
Note: Core switches obtain basic configurations such as IP addresses using the CLI. Once they establish management channels with iMaster NCE-Campus, iMaster NCE-Campus will automatically deliver services to them.

## Slide 50: DHCP-based Plug-and-Play Deployment Process
A device to be deployed obtains the NETCONF enabling status and iMaster NCE-Campus address from the DHCP server as follows:
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
  The administrator deploys the DHCP server function on the core device and configures DHCP Option 148, including the NETCONF enabling status of the device and the URL/IP address and port number of iMaster NCE-Campus.
  After the device to be deployed (SW1 in the figure) starts with empty configuration, it sends a request packet to the DHCP server through VLAN 1 (VLAN 1 is the PnP VLAN of a switch by default).
  Upon receiving the request, the DHCP server sends a DHCP packet containing Option 148 to SW1.
  SW1 registers with iMaster NCE-Campus and gets onboarded based on the information carried in Option 148 (NETCONF enabling status, URL/IP address and port number of iMaster NCE-Campus).
Core
DHCP server
SW1
Device to be deployed
1
3
2
4

## Slide 51: PnP VLAN
The Plug-and-Play VLAN (PnP VLAN) is defined for plug-and-play of switches. The default PnP VLAN of a switch is VLAN 1.
PnP VLANs consist of wired and wireless PnP VLANs, which are uniformly maintained by iMaster NCE-Campus. After a core switch registers with iMaster NCE-Campus, iMaster NCE-Campus automatically delivers the PnP VLANs preconfigured on it to the core switch.
PnP VLAN of a device to be deployed is not 1
Core
DHCP server
SW1
Device to be deployed
The core switch registers with iMaster NCE-Campus and get onboarded. iMaster NCE-Campus delivers the PnP VLANs of the devices to be deployed to the core switch.
The core switch sends the PnP VLAN (not VLAN 1) to SW1 through LLDP.
SW1 communicates with the core switch through the PnP VLAN and registers with iMaster NCE-Campus.
  The wired PnP VLAN is used to apply for the management IP address of a switch.
  The wireless PnP VLAN is used to configure the management VLAN of an AP. When a switch has an AP connected, the switch automatically changes the PVID of the interface connected to the AP to the wireless PnP VLAN ID.
  For a switch, wired and wireless PnP VLANs can be different, but they are negotiated at the same time. If only a wired PnP VLAN is configured, the PVID of the switch interface connected to an AP is changed to the wired PnP VLAN ID.
AP
Device to be deployed
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: The DHCP server pushes PnP VLAN information to its downstream devices through LLDP. Note that:
  If NETCONF is not enabled on the core switch (DHCP server), the core switch cannot be onboarded on iMaster NCE-Campus. In this case, the administrator needs to manually configure the PnP VLAN on the core switch. Then the switch to be deployed can negotiate with the core switch through LLDP to obtain the configured PnP VLAN.
Note: The PnP VLAN and management VLAN of a switch can be the same or different.
LLDP: Link Layer Discovery Protocol

## Slide 52: Network Deployment Process: Device Onboarding Before Planning
Preparations
An administrator deploys the DHCP server function on the core switch and configures DHCP Option 148.
The administrator creates a campus site on iMaster NCE-Campus.
The administrator imports switch information (ESN, device model, etc.) to iMaster NCE-Campus. (Batch import is supported.)
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
Device onboarding process
After an aggregation switch is powered on, it obtains an IP address and Option 148 from the DHCP server using the PnP VLAN ID (for example VLAN 1). The aggregation switch registers with iMaster NCE-Campus based on the iMaster NCE-Campus information obtained from the DHCP server.
After an access switch is powered on, it follows a similar process as the aggregation switch (step 1).
The access switch identifies that its downstream device is an AP and changes the PVID of the interface connected to the AP to the wireless PnP VLAN ID. The AP obtains the AC address through DHCP Option 43. After the AP is associated with the AC and VLANIF 1 is configured as the CAPWAP source interface, the AP gets onboarded on the AC.
Switches use LLDP to discover the network topology and report their topology information to iMaster NCE-Campus through NETCONF. iMaster NCE-Campus then discovers the network topology based on the received topology information.
The administrator performs network planning and configuration provisioning on iMaster NCE-Campus.
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Core (native AC)
DHCP server
Aggregation
Device to be deployed
Internet
Egress gateway
Access
Device to be deployed
AP
Device to be deployed
Notes: This deployment process applies to scenarios with scattered installation time.

## Slide 53: Network Deployment Process: Planning Before Device Onboarding
Preparations
An administrator deploys the DHCP server function on the core switch and configures DHCP Option 148.
The administrator creates a campus site on iMaster NCE-Campus.
The administrator plans the network topology using the template (an Excel file) provided by iMaster NCE-Campus and then imports the template containing the planned data to iMaster NCE-Campus.
The administrator configures the core switch so that it can be managed by iMaster NCE-Campus.
Device onboarding process
After the aggregation switch, access switch, and AP are powered on, they each complete PnP VLAN negotiation and DHCP message exchange processes, and then register with iMaster NCE-Campus.
The aggregation switch, access switch, and AP are then managed by iMaster NCE-Campus and report their LLDP neighbor information to iMaster NCE-Campus. Subsequently, iMaster NCE-Campus compares the received LLDP information with that in the network topology planning document uploaded by the administrator. If any inconsistency is found, it reports an error. In this way, the administrator can correct the topology error as prompted.
The administrator performs offline device pre-configuration on iMaster NCE-Campus. The devices automatically obtain their configurations after they are onboarded.
Core (native AC)
DHCP server
Aggregation
Device to be deployed
Internet
Egress gateway
Access
Device to be deployed
AP
Device to be deployed
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: This deployment process is applicable to scenarios with concentrated installation time. The administrator is advised to plan the network before onboarding devices. If the network cannot be planned in advance, the administrator can onboard devices first and then determine the network topology.
Network planning before device deployment and onboarding.
  During network deployment, the administrator plans the network topology by entering device ESNs and specifying stack members and aggregated links on iMaster NCE-Campus.
  Alternatively, the administrator can import the preceding planning information in batches using a template. Using a template to import data in batches simplifies operations and is therefore recommended.
  Then, the administrator uses the recommended method to deploy and onboard devices.
  After devices register with iMaster NCE-Campus, iMaster NCE-Campus automatically checks whether the actual topology of the devices is the same as the planned one. If cables are incorrectly connected during installation, iMaster NCE-Campus immediately notifies the administrator.
Note: Parameters can be planned for an Eth-Trunk interface. After a device is onboarded, it automatically obtains the corresponding Eth-Trunk configuration.

## Slide 54: Underlay Network Automation
Complete automatic deployment of the underlay network on iMaster NCE-Campus.
Border
Edge
Edge
The administrator specifies roles of fabric nodes on iMaster NCE-Campus.
iMaster NCE-Campus automatically discovers the network topology.
1
2
Border
Edge
Edge
OSPF Area 0
OSPF adjacency
3
Automatically completes OSPF configuration.
When enabling automatic routing domain configuration, you can define OSPF areas (single-area or multi-area) and configure the packet authentication function.
VLAN
IP Address
DHCP
Routing
Network Deployment
Underlay Network Automation
Notes: Automatic routing domain configuration: After this function is enabled, the underlay network can be automatically configured. You can specify sites for automatic routing domain configuration and specify OSPF routing parameters. Currently, the following parameters are supported:
  Area: In the single-area scenario, all devices belong to Area 0. In the multi-area scenario, border nodes belong to Area 0, and each edge node and its connected border node belong to an area.
  Network type: You can set the OSPF network type to broadcast, P2MP, or P2P.
  Encryption: You can set the encryption mode between adjacent devices to HMAC-SHA256, MD5, or none.
  OSPF GR: You can enable OSPF GR.
Before enabling the automatic routing domain configuration function, you need to plan network resources required for underlay network automation.
  Underlay devices (corresponding network scope of the fabric) are connected through VLANIF interfaces at Layer 3, and you need to assign a VLAN to each interconnection link.
  The VLANIF interfaces for connecting devices are automatically assigned interconnection IP addresses with a 30-bit subnet mask.

## Slide 55
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 56: Fabric Design Overview
Underlay (physical network layer)
Fabric
Fabric
External network
Network service resource
Wired access
Wireless access
Fabric design
A campus fabric is a resource pooling network abstracted from the underlay network. The fabric virtualizes underlay network resources into a resource pool to create a multi-purpose network.
The fabric design involves the following:
Fabric network resource planning
Fabric networking and node design
Design for the interconnection between the fabric and external network
Fabric network service resource planning
Fabric access management design
External network
IP/VLAN segment
Access point
VN
Network service resource
Fabric Design
Overlay Design
Notes: Fabric network resource planning:
Before creating virtual networks (VNs), you need to configure global resources, including the VLANs, VXLAN Network Identifiers (VNIs), and bridge domains (BDs). When creating a VN, iMaster NCE-Campus automatically allocates resources from the resource pools.
  Interconnection VLAN: When creating the external network resource for a fabric, configure an interconnection VLAN to interconnect the fabric with the egress network. When creating the network service resource on a fabric, configure an interconnection VLAN to interconnect the fabric with the network management zone.
  BD: BDs are used to create Layer 2 broadcast domains in a VN. Typically, BDs have a one-to-one mapping relationship with service VLANs. Therefore, a sufficient number of BD resources need to be planned to match the number of service VLANs. The default BD range is 1-4095.
  VNI: VNIs are similar to VLAN IDs. They are used to identify VXLAN segments and range from 1 to 4095 by default.

## Slide 57: Fabric Networking Scenarios
In Layer 2 or Layer 3 networking, border or edge nodes can function as gateways.
  Centralized gateway: A border node functions as the gateway to implement centralized management and simplify O&M.
  Distributed gateway: Edge nodes function as gateways to facilitate network expansion.
Recommended networking scenarios:
  Centralized gateway, VXLAN deployed across core and aggregation layers, native AC deployed on the core device, or standalone AC attached to the core device in off-path mode.
  Distributed gateways, VXLAN deployed across core and aggregation layers, native AC deployed on the core device, or standalone AC attached to the core device in off-path mode.
Networking | Border Node Location | Edge Node Location | AC Deployment Mode | Recommended
Centralized gateway | Core | Access | Native AC on the core device | No
 |  |  | Standalone AC attached to the core device in off-path mode | No
 |  | Aggregation | Native AC on the core device | Yes
 |  |  | Standalone AC attached to the core device in off-path mode | Yes
Distributed gateway | Core | Aggregation | Native AC on the core device | Yes
 |  |  | Standalone AC attached to the core device in off-path mode | Yes
 |  | Access | Standalone AC attached to the core device in off-path mode | No
Fabric Design
Overlay Design

## Slide 58: Fabric Networking Design: VXLAN Coverage Range
Core layer
Aggregation layer
Access layer
VXLAN
VXLAN
CAPWAP
CAPWAP
VXLAN range | VXLAN across core and access layers | VXLAN across core and aggregation layers
Application scenarios | Automatic end-to-end service deployment is required on the entire network. Recommended: Number of switch nodes < 1,000 | Existing access switches on the live network need to be reused. Alternatively, low-cost Huawei switches that do not support VXLAN need to be deployed at the access layer to reduce costs. Recommended: Number of switch nodes < 3,000
Network construction costs | Compared with the VXLAN solution from the core layer to the aggregation layer, this solution has higher network construction costs. | Compared with the VXLAN solution from the core layer to the access layer, this solution has lower network construction costs.
VXLAN not supported
VXLAN not supported
Fabric Design
Overlay Design

## Slide 59: Fabric Networking Design: Centralized and Distributed Gateways
Layer 3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
Layer 2 gateway
Layer 2 gateway
PC2
192.168.2.1/24
The Layer 3 gateway is deployed on a single device. All inter-subnet traffic is forwarded by the gateway to implement centralized traffic management.
Advantage: Inter-subnet traffic is managed in a centralized manner, simplifying gateway deployment and management.
Disadvantage: The forwarding path is not optimal.
Layer 3 gateways are deployed on multiple devices, and VTEPs function as both Layer 2 and Layer 3 gateways.
Advantage: The forwarding path of inter-subnet traffic is optimal.
Disadvantage: Gateway deployment, fault locating, and network O&M of the distributed gateway networking are more complex than those of the centralized gateway networking. VTEPs need to exchange and maintain host routes.
Centralized gateway (recommended)
Distributed gateway
Layer 2/3 gateway
Layer 2/3 gateway
PC1
192.168.1.1/24
PC3
192.168.1.3/24
PC2
192.168.2.1/24
Fabric Design
Overlay Design
Notes: In large- and medium-sized campus networks, the virtualization solution is classified into the centralized gateway solution and distributed gateway solution based on the user gateway location. You can select a gateway solution when creating a fabric on iMaster NCE-Campus.
In the centralized gateway solution, a border node functions as the gateway of all users, and all inter-subnet traffic is forwarded by the border node. In the distributed gateway solution, multiple edge nodes function as user gateways, and inter-subnet traffic is forwarded through these edge nodes.

## Slide 60: Fabric Networking Design: Gateway Solution Selection
Item | Centralized Gateway | Distributed Gateway
User gateway location | Border | Edge
Recommended edge location | Aggregation switch | Aggregation switch
O&M deployment | The border node functions as the gateway of all users, and the native AC function is typically enabled on the border node to support wireless services. | Multiple edge nodes function as user gateways. This ensures that only part of the network is affected upon the failure of one gateway and facilitates network expansion. The native AC function is enabled on the border node to support wireless services.
Terminal scale | ≤ 50000 (calculated based on the number and specifications of centralized gateways). This solution is recommended when the number of terminals does not exceed 50000. | ≤ 100000 (calculated based on the number and specifications of distributed gateways). This solution is recommended when the number of terminals exceeds 50000.
Core layer
Aggregation layer
Access layer
VXLAN
VXLAN
CAPWAP
CAPWAP
VXLAN not supported
VXLAN not supported
Fabric Design
Overlay Design
VXLAN not supported
VXLAN not supported
Notes: When designing the CloudCampus network virtualization solution, first determine the gateway solution to be used. Then you can perform end-to-end design for the entire campus network based on the selected gateway solution.
The centralized gateway solution supports only one border node, whereas the distributed gateway solution supports multiple border nodes.

## Slide 61: Fabric Node Design: Single-Border Networking
Core layer design:
  Deploy a cluster of core switches or a single core switch. It is recommended that large-capacity modular switches set up a cluster and S12700E series switches be used as core switches.
  It is recommended that ENP cards be used for interconnection with aggregation switches and that Eth-Trunk be deployed.
Aggregation layer design:
  Deploy a stack of aggregation switches or a single aggregation switch. It is recommended that a cluster of modular switches or a stack of fixed switches be deployed. Large-capacity switches (S12700E or S6700 series switches) are recommended.
  Eth-Trunk is recommended for interconnection with the core layer and access layer.
Access layer design:
  Wired access node: Each node can be a stack or a single device.
  Wireless access node: Fit AP
Server zone design:
  It is recommended that iMaster NCE-Campus, analyzer, and DHCP server be connected to the campus network through switches in the server zone.
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
DHCP server
Server zone
Border
Fabric Design
Overlay Design
Notes: An Ethernet Network Processor (ENP) card is embedded with the Huawei-developed ENP. The card can function as a common LPU to provide data access and switching services and also as a WLAN AC to provide wireless access control functions. In this way, the card achieves wired and wireless convergence.

## Slide 62: Fabric Node Design: Dual-Border Networking
Core layer design:
  Core switches are two logical devices. Large-capacity switches (S12700E series switches) are recommended. It is recommended that ENP cards be used for interconnection with aggregation switches and that Eth-Trunk be deployed.
Aggregation layer design:
  It is recommended that aggregation switches set up a stack to implement load balancing with core switches.
Access layer design:
  The design is similar to that in the single-border networking scenario.
Server zone design:
  It is recommended that iMaster NCE-Campus, analyzer, and DHCP server be connected to the campus network through switches in the server zone.
Core layer
Access layer
Egress zone
DHCP server
Server zone
Border
Border
Aggregation layer
CSS/iStack link
Load balancing
Load balancing
Load balancing
Fabric Design
Overlay Design

## Slide 63: Fabric Node Design: Single/Dual-Border Networking Selection
 | Single-Border Networking | Dual-Border Networking
Description | The core switch is a logical device, which can be a physical standalone device or a CSS/iStack system. | Core switches are two logical devices, which can be two standalone physical devices or two CSS/iStack systems.
Characteristics | Easy management, configuration, and maintenance. Services may be affected during the device upgrade. | Complex management, configuration, and maintenance. The upgrade of core switches has little impact on services.
Application scenario | Simple network management, configuration, and maintenance are required. | The device upgrade has little impact on services. Core switches do not support clustering or stacking due to some reasons (such as the deployment distance).
Restrictions | There is no restriction. The single-border networking design is applicable to both centralized and distributed VXLAN gateway networking. | The dual-border networking design is applicable only to distributed VXLAN gateway networking.
Fabric Design
Overlay Design

## Slide 64: Design for the Interconnection Between the Fabric and External Network
L3 shared egress
Application scenario:
Multiple VNs on a fabric share a Layer 3 egress, through which they communicate with the egress device, and these VNs use the same security policies.
VRF
VRF
VRF
Shared VRF
Green VRF
VN1
Red VRF
VN2
Border
Trust zone
L3 exclusive egress
Application scenario:
Each VN on the fabric network exclusively occupies a Layer 3 egress, through which it communicates with the egress device, and each VN uses differentiated security policies.
VRF
Green VRF
VN1
Border
VRF
Red VRF
VN2
Trust zone
Red zone
(User-defined zone)
L2 shared egress
Application scenario:
The border node does not function as the user gateway, and the user gateway must be located outside the fabric.
Edge1
Border
L2 shared port
Edge2
Trust zone
User gateway
Fabric Design
Overlay Design
Notes: When the campus intranet needs to communicate with an external network, for example, the Internet, data center, or another branch, traffic must pass through the border node.
There are three interconnection modes between the fabric network and egress device:
  L3 shared egress:
    The external gateway connects to and accesses external networks via VLANIF or VBDIF interfaces. VNs can access the public network or private network specified by another site through the shared VRF egress, and service traffic can be diverted to the firewall through the shared VRF egress. When configuring a multi-border fabric, you can configure multiple core devices in one external network.
    The L3 shared egress mode is applicable to the scenario where the firewall does not need to perform security check on VNs, there are low requirements on security control policies between VNs, and traffic of all VNs is transmitted in the same security zone.
    To enable communication between VNs and external networks, you must configure return routes to service subnets on the firewall. As a result, service subnets of different VNs can communicate with each other on the firewall. To isolate VNs on the firewall, configure policies based on service network segments in the VNs.
    As shown in the figure, a shared VRF is created on the border node, the shared L3 egress is bound to the VRF, and routes are configured to enable the communication with external networks.

## Slide 65
Notes:   L3 exclusive egress:
    The external gateway connects to and accesses external networks via VLANIF or VBDIF interfaces. The service VRF (VRF corresponding to a VN) is used as the egress VRF of the external gateway. Tenant traffic is directly sent out through the service VRF. When configuring a multi-border fabric, you can configure multiple core devices in one external network.
    The L3 exclusive egress mode applies to scenarios where the firewall needs to perform security check on VNs, there are high requirements on security control policies between VNs, and VN traffic is transmitted in multiple security zones.
    In this scenario, multiple security zones can be configured on the firewall, each corresponding to one L3 exclusive egress. Thus, the traffic of service subnets of different VNs is isolated when reaching the firewall. To enable inter-VN communication through the firewall, you can configure inter-zone security policies to control the application ports used for the communication and limit the bandwidth.
    As shown in the figure, a VRF on the border node is associated with a VN. The VRF for the VN that needs to access an external network is bound to an L3 egress, and routes are configured for each VN that needs to access an external network to enable the communication between the VN and external network.
  L2 shared egress:
    The user gateway is located outside the fabric. Service traffic is transparently transmitted from the fabric to external networks through the L2 shared egress. That is, the border node connects to the egress device through a Layer 2 interface, and the user gateway is deployed on the egress device for access to external networks.
    The L2 shared egress mode applies to the scenario where the user gateway is located outside the fabric. In higher education scenarios, if a Broadband Remote Access Server (BRAS) is used as the user authentication point and PPPoE dialup is required on the network, the L2 shared egress mode can be used.
Communication between a fabric and external network can be implemented through static routes, BGP routes, BGP4+ routes, or OSPF routes.

## Slide 66: Network Service Resource Planning for a Fabric
In the network service resource design for the fabric, network service resources are created on the border node so that service terminals on the campus intranet can access service resources, such as the DHCP server and NAC server, in the network management zone.
Three models are available for the network service resource design, depending on the resource deployment location.
Directly connected to a server
The border node is directly connected to the network service resource, and the interconnection interface on the border node is added to the interconnection VLAN in untagged mode.
Directly connected to a switch
DHCP server deployed on an external network
The border node is connected to the network service resource through a switch, and the interconnection interface on the border node is added to the interconnection VLAN in tagged mode.
The border node is connected to the network service resource over an external network.
VN1
Border
DHCP Server
Access port
Trunk port
Egress
Gateway in the network management zone
Network service resource
VN1
Border
DHCP Server
Egress
Network service resource
VN1
Border
Egress
DHCP Server
External network/
Network service resource
Fabric Design
Overlay Design
Notes: Multiple network service resources can be created, or a network service resource can have access addresses for multiple network service resources.
When the border node is directly connected to a server:
  As shown in the figure, a VRF on the border node is allocated to each network service resource. After a network service resource is selected during VN creation, a static route pointing to the network service resource address will be created on the border node, with the next hop being the network service resource address.
When the border node is directly connected to a switch:
  If the DHCP server, iMaster NCE-Campus, and other network service resources are all deployed in the network management zone, the border node communicates with these network service resources through the directly connected switch (gateway) in the network management zone. If only a small number of network service resources are deployed, it is recommended that these resources be planned in the same network service resource model. This saves interconnection VLAN and IP address resources and simplifies route configuration in the network management zone.
  As shown in the figure, a VRF on the border node is allocated to each network service resource. After a network service resource is selected during VN creation, a static route pointing to the network service resource address will be created on the border node, with the next hop being the address of the gateway in the network management zone.

## Slide 67
Notes:   Note: Routes on the border node are automatically delivered when network service resources are created on iMaster NCE-Campus. To configure routes on the gateway in the network management zone, log in to the web system or CLI of the gateway device.
When the DHCP server is deployed on an external network:
  This network service resource model is mainly used for obtaining the DHCP server address. When this model is used, the gateway of the VN subnet can function as the DHCP relay agent and automatically configure the DHCP server address after the gateway is created.
  As shown in the figure, after the external network and network service resource are selected during VN creation, the Layer 3 egress on the border node is bound to the VRF of the VN, and a route pointing to the external network is created, enabling the VN to access the network service resource.
Note: The models shown on this page are logical connectivity diagrams. The actual connections are subject to the actual networking.

## Slide 68: Access Management Design for a Fabric
When creating a fabric, you need to design authentication control points for user access, including planning access point resource pools. Wired access point resources refer to switch interfaces to which terminals connect, whereas wireless access point resources refer to SSIDs with which terminals associate. In the centralized gateway solution:
  You are advised to deploy authentication control points for wired users on the edge nodes and plan this during access management configuration for a fabric.
  The authentication control points for wireless users are deployed on the ACs. The design and planning for this type of authentication control point depend on the AC type.
VXLAN
Border
Edge
Edge
Fabric extended switch
Fabric extended AP
Terminal
Access interface design
During access management configuration for a fabric, three connection types are defined for access interfaces on a switch.
Fabric extended AP: The interface connects to a Huawei Fit AP.
Fabric extended switch: The interface connects to a Huawei switch.
Terminal (PCs, phones, dumb terminals, and non-fabric extended access switches or APs): The interface connects to a terminal or switch/AP (when policy association is not deployed).
Fabric Design
Overlay Design
Notes: "Fabric extended AP" and "Fabric extended switch": The two types of connections are used to enable communication between the authentication control point and authentication enforcement point through the policy association management VLAN. In this scenario, the fabric extended switch functions as the authentication enforcement point and can be connected to fabric extended APs and terminals.
Terminal (PCs, phones, dumb terminals, and non-fabric extended access switches/APs): If this type of interface is connected to a terminal, you can associate an authentication profile specific to that terminal type with the terminal based on the user authentication mode design in the access control design. Binding the authentication profile facilitates access control of the terminal.

## Slide 69: VN Design Process
Fabric
VN1: OA network
VN2: R&D network
VN3: production network
VN design
Create multiple VNs based on the fabric.
Policy design
Divide users into security groups and define inter-group policies (policy control matrix).
Define inter-VN access policies based on the policy control matrix.
VN access design
Plan the mapping between VLANs of physical networks and BDs of VNs.
Plan terminal access modes.
VN1: OA network
VN2: R&D network
VN3: production network
VIP
Sales
Guest
Marketing
Testing
Code library
Server
Operations
…
…
Server
Programmer
VN1: OA network
VN2: R&D network
VN3: production network
5W1H
5W1H
5W1H
1
2
3
Security groups
Security groups
Security groups
Fabric Design
Overlay Design
Notes: VN design:
  VNs are generally divided based on services on a campus network. An independent service is assigned a VN, and VNs are isolated from each other by default. For example, on a school campus network, guest, teaching, IoT, and video surveillance services can each be assigned a separate VN. On an enterprise campus network, office network services, production network services, and R&D services can be allocated to different VNs.
Policy design:
  Some isolation requirements caused by different user roles can be fulfilled by deploying policy control technologies (such as free mobility).
  VNs are isolated by default. To enable mutual access between user groups within a VN, additional VN interworking configuration is required.
VN access design:
  Service data enters from a physical network to a VN through an edge node. Service data of users enters different VNs depending on the VLANs to which users belong. Therefore, during network design, you need to plan the mappings between VLANs of physical networks and BDs of VNs, and configure VLANs for wired and wireless users.

## Slide 70
Notes: 5W1H:
  Who: identity of an access user, for example, a company leader, a common employee, or a guest.
  Where: user access location, for example, access from within the campus, or remote access.
  What: type of the terminal used by the access user, for example, mobile phone or PC/laptop.
  When: time when a user accesses the network, for example, whether the user accesses the network in the daytime or at night.
  Whose: device owner, for example, whether the device is company-issued or BYOD.
  How: access mode of a user, for example, wired or wireless access.

## Slide 71: VN Design
Overlay (virtual network layer)
VN 1
VN 2
VN 3
VRF+VNI
VRF+VNI
VRF+VNI
1. Network service abstraction
Physical network resources are pooled through orchestration, and the network is abstracted into Fabric as a Service (FaaS). A VN is a FaaS instance and includes:
IP/VLAN segment
External network
Network service resource: The IP/VLAN segment is the capability provided by the VN for clients to use network resources.
Access point: Terminals access VNs through access points.
2. Network service orchestration
Deliver the mappings between VNIs and BDs.
Deliver the mappings between BDs and VLANs.
Deliver the IP address segments corresponding to VBDIF interfaces.
Deliver VRFs and bind them to VBDIF interfaces.
Deploy VNs
Underlay (physical network layer)
Fabric
Fabric
External network
Network service resource
Wired access
Wireless access
External network
IP/VLAN segment
Access point
VN
Network service resource
Deliver configurations
Fabric Design
Overlay Design

## Slide 72: VN Access Design
Service data enters from a physical network to VNs through the edge node. Service data of different users enters different VNs depending on the VLANs to which the users belong.
Wired user traffic is directly transmitted to VNs based on VLANs. After wireless user traffic is forwarded to the native AC, the native AC decapsulates CAPWAP packets and forwards the packets to the corresponding BDs based on the VLANs.
Static VLANs
VN1
VN2
A static VLAN is configured for wired users on an interface of an access switch.
A static service VLAN is configured for wireless users on an SSID.
Native AC
Configure a static VLAN
Deliver the static
service VLAN
Dynamically authorized VLANs
VN1
VN2
Authorized VLANs of wired users are delivered to the corresponding authentication points, which then send received user traffic to different VLANs.
Authorized VLANs of wireless users are delivered to the corresponding native ACs, which then send received user traffic to different VLANs.
Deliver the authorized user VLAN
Deliver the authorized user VLAN
Native AC
Fabric Design
Overlay Design
Notes: Application scenarios:
  The static VLAN mode applies when terminals access the network at fixed locations and do not need to be authenticated. This access mode is more secure but lacks flexibility. When the locations of terminals change, you need to configure static VLANs for them again.
  The dynamically authorized VLAN mode applies when terminals need to access the network from any place and need to be authenticated based on the VLAN information delivered during user authentication. This access mode is flexible and the configuration does not need to be modified when the locations of terminals change. Dynamic access is more automated, easy to manage and use, and is therefore recommended.
VN access design for wireless users:
  If distributed gateways are used and the border nodes have the native AC function deployed, traffic of wireless users is forwarded to the native AC through CAPWAP tunnels. After the native AC decapsulates CAPWAP packets, the decapsulated packets enter different VNs depending on the VLANs to which the wireless users belong.
  If centralized gateways are used and the border nodes have the native AC function deployed, it is recommended that traffic of wireless users be directly forwarded to the native AC through CAPWAP tunnels. After the native AC decapsulates CAPWAP packets, the decapsulated packets enter different VNs depending on the VLANs to which the wireless users belong. The administrator needs to configure different VLAN ranges for wired and wireless terminals. The VLANs of wired terminals are bound to BDs on the edge nodes, whereas the VLANs of wireless terminals are bound to BDs on the border nodes.
Note: 802.1X authentication and MAC address authentication both support dynamically authorized VLANs.

## Slide 73: Inter-VN Communication Design
Inter-VN communication through a border node (centralized gateway scenario)
Inter-VN communication through an external gateway
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
Traffic for inter-VN communication is forwarded through the border node. VRFs on the border node need to import routes from each other.
This mode applies to the scenario where two VNs belong to the same security zone and there are low security control requirements.
Traffic for inter-VN communication is forwarded to the border node and then diverted to the external gateway. Subsequently, the external gateway performs a security check or forwards the traffic back to the border node, which then forwards the traffic to the destination.
This mode applies to the scenario where two VNs belong to different security zones and there are high security control requirements (for example, application-based policy control).
VRF1 and VRF2 on the border node import each other's network segment routes.
Border
Host 1
10.1.1.1/24
Host 2
10.2.2.2/24
VTEP1
1.1.1.1
VTEP2
2.2.2.2
VBDIF 10.1.1.254
VBDIF 10.2.2.254
VNI 1000
VNI 1001
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
VRF1
(L3VNI 1000)
VRF2
(L3VNI 1001)
Firewall
Fabric Design
Overlay Design
Notes: Inter-VN communication can be implemented through a border node or an external gateway.
  Through a border node
    If two VNs belong to the same security zone and have low security control requirements, devices on the two VNs can directly communicate with each other through a border node. In addition, permission control can be implemented based on the free mobility policy. To implement communication between VNs, the border node needs to import their respective network segment routes that are reachable to each other.
  Through an external gateway
    If two VNs belong to different security zones and have high security control requirements, it is recommended that devices on the two VNs communicate through an external gateway (a firewall) and that a security zone policy be configured on the firewall for permission control.

## Slide 74: Mapping Between the Logical Network and Physical Network
Border
Edge
Edge
Router
R&D
Production
OA
VNs
Router
Border
Edge
Zone1
Zone2
Zone3
Security policy
Zone4
IP packet
V
R
F
1
V
R
F
2
V
R
F
3
Public
VLAN
VLAN
VLAN
VLAN
VLAN
VLAN
VXLAN Tunnel
VBDIF: Layer 3 VXLAN gateway interface
IP packet
IP packet
IP packet
IP packet
FW
Traffic of end users
Fabric Design
Overlay Design
Notes: Each VN corresponds to a VRF.
Each VN corresponds to multiple subnets, and each subnet corresponds to a BD and VNI.
Traffic from a terminal enters the VN based on the VLAN to which the terminal belongs.

## Slide 75
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 76: User Management Solution Design
User management solution design involves confirming the user data source server. Typical user data source servers of enterprises include RADIUS, AD, and LDAP servers.
Confirm the user data source server
RADIUS server
AD server
LDAP server
If an enterprise has no data source server, it is recommended that Huawei iMaster NCE-Campus be used as the data source server.
If an enterprise has used the AD/LDAP server as the user data source server, the enterprise can continue to use the legacy AD/LDAP server. iMaster NCE-Campus can synchronize user data with such a server and finally perform network authorization.
Same principles as the AD server
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 77: User Authentication Technology Selection
Common authentication technologies include 802.1X, MAC address, and Portal authentication. The following table compares these authentication methods.
Item | 802.1X Authentication | MAC Address Authentication | Portal Authentication
Client required or not | Required | Not required | Not required
Advantage | High security | No need to install a client | Flexible deployment
Disadvantage | Inflexible deployment | MAC addresses need to be registered, complicating management | Low security
Application scenario | Network authentication of office users with high security requirements | Access authentication of dumb terminals such as printers and fax machines | Network authentication of guests who move frequently and use different types of terminals
On large- and medium-sized campus networks, 802.1X authentication is recommended for employees, Portal authentication for guests, and MAC address authentication for dumb terminals.
If a customer wants to use more than one authentication method on the same access point, a combination of authentication methods (hybrid authentication) can be used. After hybrid authentication is configured, terminals can access the network after passing any authentication in the combination. This mode is applicable to scenarios where one port provides access for multiple types of users. For example, if a PC is connected upstream to an IP phone, you can configure hybrid authentication (MAC address authentication + 802.1X authentication). In this way, the IP phone uses MAC address authentication, and the PC uses 802.1X authentication.
User Management
User Authentication
Policy Control
Terminal Identification
Notes: If 802.1X or MAC address authentication (Layer 2 authentication technologies) is used, the authentication point must be on the same network segment as the user host. It is recommended that the access device function as the authentication point.
  If a large number of access devices are deployed, the aggregation or core device needs to be deployed as the authentication point. You can also deploy policy association. The gateway functions as the authentication control point, and the access device functions as the authentication enforcement point, thereby simplifying policy deployment.
If Portal authentication is used, the authentication point can be deployed anywhere as long as it is routable to the user host. Layer 2 Portal authentication is recommended.

## Slide 78: Association Between Authenticated Users and VNs
1. Create VNs on iMaster NCE-Campus.
2. Authenticated users obtain authorized VLANs and are then associated with VNs based on the VLANs.
The administrator creates VNs and specifies the IP network segments and VLANs for the VNs.
The administrator configures user authentication rules, authorization results, and authorization rules, so that users can obtain corresponding VLANs after being authenticated. For example, the administrator configures user test to obtain the authorized VLAN 10 after passing 802.1X authentication.
OA VN
VLAN 10: 10.1.10.0/24
VLAN 20: 10.1.20.0/24
R&D VN
VLAN 30: 10.1.30.0/24
VLAN 40: 10.1.40.0/24
1
User test attempts to access the network.
Send an authentication request.
Issue the authorization result (VLAN 10) after successful user authentication.
2
3
4
User Test accesses the OA VN.
test
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 79: Multi-Level Design for Access Policies
Network access policies can be logically divided into two levels:
  VN-level access policy: By default, VNs cannot communicate with each other, and service data of each VN is isolated. The CloudCampus Solution enables VNs to communicate within a fabric or through an external network.
  Security group-level access policy: Users and network resources are divided into different security groups for efficient management and control of inter-group traffic. The free mobility policy enforcement point executes inter-group access policies.
Fabric
HR group
R&D group
Guest group
Internet
OA server resource group
OA VN
R&D VN
R&D group 1
Sensitive data
resource group
HR server resource group
R&D code library
resource group
R&D group 2
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 80: Policy Design: Create Security Groups
Dynamic security groups: Terminals and users accessing the network are divided into different security groups through NAC authorization.
  Define security groups for enterprise employees based on the enterprise organizational structure.
  Define a security group for a special group of people in the organizational structure, such as the VIP group.
  Define a security group for non-employees that access the network, such as the guest group.
  Define a security group for dumb terminals connected to the network, such as printers and access control devices.
Hardware development Dept.
Software development Dept.
Testing Dept.
Financial Dept.
Human resources Dept.
Marketing Dept.
Dynamic security groups are authorized based on the 5W1H principle.
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 81: Policy Design: Create Resource Groups
Static resource groups: Configure a group of IP address resources as a static resource group.
  Define security groups, such as the OA resource group and R&D resource group, for intranet resources based on security requirements.
  If Internet access control is required, define an Internet resource group.
Aggregate the IP addresses of dispersed data center applications into a resource group, thereby simplifying deployment.
Internet
Internet resource group
General office resources, such as websites and email addresses
OA resource group
Internal private applications, files, code, etc.
R&D resource group
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 82: Policy Design: Design the Policy Control Matrix
Create dynamic and static security groups for free mobility based on actual requirements, and design the policy control matrix based on network access permissions.
Dynamic security groups
HR
R&D
Sales
Guest
Static security groups
OA server
R&D code library
Marketing document library
Internet
 | OA server | R&D code library | Marketing document library | Internet | HR | R&D | Sales | Guest
HR | Permit | Deny | Deny | Permit |  | Permit | Permit | Deny
R&D | Permit | Permit | Deny | Permit | Permit |  | Permit | Deny
Sales | Permit | Deny | Permit | Permit | Permit | Permit |  | Deny
Guest | Deny | Deny | Deny | Permit | Deny | Deny | Deny | 
Source
Destination
Policy control matrix:
User Management
User Authentication
Policy Control
Terminal Identification
Notes: An inter-group policy directly reflects whether two security groups can communicate with each other. When planning an inter-group policy, simply set the inter-group policy to permit or deny based on whether the two groups can communicate with each other. The administrator can configure inter-group policies through an intuitive policy control matrix on iMaster NCE-Campus. If no inter-group policy is created between source and destination security groups, the default policy between them is permit.
Take the policy direction into account when planning inter-group policies. Typically, packets are transmitted in two directions between two terminals.
  Huawei switches consider that traffic from A to B is unrelated to traffic from B to A, so they match policies for the two types of traffic separately and determine whether to forward the traffic based on the corresponding policies. This means that a Huawei switch enforces policies on a packet by considering only the source and destination security groups of that packet. For example, the policy "A ->B permit, B -> A deny" means that all packets sent from A to B will be permitted, whereas all packets sent from B to A will be discarded, regardless of whether A or B initiates the access. The default inter-group policy on a switch is permit.

## Slide 83: Location Selection for Authentication Points and Policy Enforcement Points
Typically, the user gateway functions as both an authentication point and policy enforcement point, on which the free mobility function is deployed, due to the following considerations:
  There are a large number of access switches. Configuring the authentication function on each access switch brings a heavy workload and leads to difficulties in management.
  iMaster NCE-Campus needs to synchronize permission control policies to policy enforcement points. If access switches are used as authentication points, the number of policy enforcement points will increase significantly due to the large number of access switches. This increases the workload and difficulty in device management on iMaster NCE-Campus and prolongs the policy synchronization time as well.
To prevent users connected to the same upstream user gateway from communicating with each other at Layer 2, you can configure Layer 2 isolation. In this way, traffic between these users must pass through the user gateway.
User Management
User Authentication
Policy Control
Terminal Identification
Notes: If an authentication point and policy enforcement point are deployed on different devices, the IP-security group entries of authenticated users need to be pushed to the specified policy enforcement point. To achieve this, the administrator needs to configure IP-security group entry subscription, that is, specify to which policy enforcement point the IP-security group entries of a certain network segment or security group need to be pushed.

## Slide 84: IP-Security Group Entry Synchronization
Technical background
IP-security group entry synchronization principle
iMaster NCE-Campus synchronizes the mappings between user IP addresses and security groups to the switches functioning as policy enforcement points. In this way, authentication points and policy enforcement points can be separated, thereby implementing flexible networking. In addition, hybrid networking with third-party devices can be easily achieved.
1
3
IP | Group
1.1.1.1 | Group1
2.2.2.2 | Group2
PC1 1.1.1.1
PC2 2.2.2.2
User access
2
User authentication
4
Proactively synchronize IP-security group entries through HTTP/2.
5
Enforce the inter-group policy when the traffic arrives.
Third-party device
These devices do not support free mobility, so how to realize free mobility if a solution includes these devices?
Switches that do not support free mobility
ACs
Routers
Third-party devices (non-Huawei)
Free mobility supported
Free mobility not supported
Generate an IP-security group entry.
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 85: Free Mobility Solution (1)
Scenario description
Centralized authentication point + centralized policy enforcement point.
The authentication point and policy enforcement point are combined on the core device.
Devices do not support VXLAN.
Scenario characteristics
The core device functions as the centralized authentication point for both wired and wireless users on the entire network.
The core device also works as the policy enforcement point for free mobility.
The core device stores authentication information about all users on the network. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by the administrator.
The network does not need to support or deploy VXLAN.
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
Core
AGG1
AGG2
Access1
Access2
PC2 2.2.2.2
R&D user
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Security group
Security group-based policy control matrix
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 86: Free Mobility Solution (2)
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Core
AGG1
AGG2
Access1
Access2
Security group
Security group-based policy control matrix
Scenario description
Distributed authentication points + centralized policy enforcement point.
Authentication points are separated from the policy enforcement point.
Devices do not support VXLAN.
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
The core device functions as the centralized policy enforcement point for free mobility.
iMaster NCE-Campus synchronizes IP-security group entries to the core device. After traffic is forwarded to the core device, it enforces policies based on the policy control matrix defined by the administrator.
The network does not need to support or deploy VXLAN.
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
IP Address | Group ID
1.1.1.1 | 1
2.2.2.2 | 2
3.3.3.3 | 3
… | …
IP-security group mapping table
Synchronize IP-security group entries
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
Device enabled with IP-security group
entry subscription
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 87: Free Mobility Solution (3)
Core
AGG1
AGG2
Access1
Access2
Scenario description
VXLAN-based virtualized campus network, with automatic service provisioning.
Distributed authentication points + policy enforcement points.
Scenario characteristics
Multiple authentication points exist on the entire network, for example, distributed on aggregation switches.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
VXLAN
PC1 1.1.1.1
Sales user
PC3 3.3.3.3
Marketing user
PC2 2.2.2.2
R&D user
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Group Name | Group ID
Sales | 1
R&D | 2
Marketing | 3
… | …
 | Sales | R&D | Marketing | …
Sales | √ | × | √ | …
R&D | × | √ | √ | …
Marketing | √ | √ | √ | …
… | … | … | … | …
Security group
Security group-based policy control matrix
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 88: Free Mobility Solution (4)
Host1
Sales user
A-Agg
B-Agg
B-Access
1
2
3
4
5
AP
A terminal attempts to go online and initiates authentication.
Authenticate the user.
Generate an IP-security group entry.
Deliver the IP-security group entry.
Enforce the inter-group policy when the traffic arrives.
Device enabled with IP-security group
entry subscription
A-Access
(third party)
Host4
Guest
Scenario description
VXLAN-based virtualized campus network.
Distributed authentication points + policy enforcement points.
The third-party device functions as a user authentication point.
Scenario characteristics
A third-party switch exists on the network and functions as a user authentication point.
Aggregation switches support VXLAN and function as policy enforcement points.
The policy for traffic exchanged between users on the same aggregation switch is enforced by the aggregation switch itself.
Traffic exchanged between users on different aggregation switches is encapsulated using VXLAN. The source security group ID is encapsulated into VXLAN-encapsulated traffic. Policies are enforced on the peer aggregation switch.
VXLAN
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Synchronize IP-security group entries
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 89: Free Mobility Solution (5)
Scenario description
VXLAN-based virtualized campus network
The AC functions as the authentication point for wireless users, and the core switch functions as the gateway for wireless users.
Scenario characteristics
The AC functions as the authentication point for wireless users and interacts with iMaster NCE-Campus to complete user authentication.
The core switch functions as the free mobility policy enforcement point, to which iMaster NCE-Campus synchronizes IP-security group entries.
Core
VXLAN
AC
Device enabled with IP-security group
entry subscription
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Synchronize IP-security group entries
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 90: Free Mobility Solution (6)
User Management
User Authentication
Policy Control
Terminal Identification
Scenario description
VXLAN-based virtualized campus network.
The third-party device (BRAS) functions as the user authentication point, and terminals need to access the external network after PPPoE authentication. Free mobility is supported.
Scenario characteristics
The third-party BRAS functions as the user authentication point and interacts with iMaster NCE-Campus to complete user authentication.
iMaster NCE-Campus automatically provisions VXLAN configurations, so that VXLAN tunnels can be created for transmitting user authentication data to the BRAS, thereby enabling Layer 2 communication between terminals and the BRAS.
The L2 shared egress mode is configured on the core switch through iMaster NCE-Campus for the connection between the fabric and the external network, so that the core switch can communicate with the third-party BRAS.
The core switch functions as the free mobility policy enforcement point, to which iMaster NCE-Campus synchronizes IP-security group entries.
VXLAN
Third-party BRAS
PPPoE authentication
VXLAN tunnel
Authentication point
Policy enforcement point
Security group and policy control matrix delivery
Synchronize IP-security group entries
Core
Device enabled with IP-security group
entry subscription
Notes: L2 shared egress mode: The border node is not the user gateway, and the user gateway is a device outside the fabric. The border node connects to the egress device through a Layer 2 interface, and the user gateway is deployed on the egress device for access to the external network.

## Slide 91: Terminal Identification Method Design (1)
iMaster NCE-Campus allows you to view brief information about terminals on the entire campus network, such as terminal types and operating systems, thereby enabling multi-dimensional refined management of terminals. For dumb terminals such as IP phones, printers, and IP cameras on the campus network, automatic access based on terminal identification results can be implemented, thus reducing the configuration workload of administrators.
To view terminal types and perform network management based on the terminal type through iMaster NCE-Campus, a network administrator needs to perform the following operations:
Collect the types of terminals on the network, such as PCs, mobile phones, printers, IP cameras, and access control devices.
Determine whether Portal authentication is deployed on the network.
Check whether the IP addresses of terminals are DHCP-assigned or statically configured.
Network analysis
Identification Method | Identifiable Terminal Type | Application Scenario
MAC OUI | All IP terminals (identifying only the device manufacturer) | General scenarios
HTTP User-Agent | Mobile phones, tablets, PCs, workstations, smart audio and video terminals | Only scenarios where Portal authentication is used for terminals
DHCP Option | Mobile phones, tablets, PCs, workstations, IP cameras, IP phones, printers, etc. | Only scenarios where IP addresses of terminals are dynamically assigned
LLDP | IP phones, IP cameras, network devices, etc. | General scenarios
mDNS | Printers, IP cameras, etc. | General scenarios
SNMP Query | Network devices, printers | On-premises scenario
Nmap | PCs, workstations, printers, phones, IP cameras, etc. | On-premises scenario
Traverse items in the following table one by one
Based on the collected information, traverse the items listed in the following table one by one and select the required terminal identification methods. (All the identification methods that meet requirements must be enabled.)
1
2
User Management
User Authentication
Policy Control
Terminal Identification
Notes: In this slide, "general scenarios" refer to authentication, non-authentication, and dynamic/static IP address assignment scenarios.
In non-authentication scenarios, iMaster NCE-Campus can display information about wired terminals only after the ARP snooping function is enabled on access devices.

## Slide 92: Terminal Identification Method Design (2)
If the network administrator cannot determine the terminal identification method to be used, the following passive fingerprint-based identification methods are recommended: MAC OUI, HTTP User-Agent, DHCP Option, LLDP, and mDNS.
It is recommended that Nmap be disabled by default because this identification takes a long time. If the passive fingerprint-based identification methods cannot meet requirements, enable Nmap.
Enable the terminal identification function
Identification Method | Operation On iMaster NCE-Campus | Operation on the Network Side
MAC OUI | Enable the terminal identification function. | -
HTTP User-Agent | Enable the terminal identification function. | Enable the terminal identification information reporting function.
DHCP Option | Enable the terminal identification function. | Enable the terminal identification information reporting function. Enable DHCP snooping.
LLDP | Enable the terminal identification function. | Terminal identification is enabled by default.
mDNS | Enable the terminal identification function. | Enable the terminal identification information reporting function. Enable mDNS snooping.
SNMP Query | Enable the terminal identification function. Enable the SNMP scanning function. | -
Nmap | Enable the terminal identification function. Install the Nmap plug-in. | -
3
User Management
User Authentication
Policy Control
Terminal Identification

## Slide 93: Terminal Policy Design
The network administrator can use iMaster NCE-Campus to automatically deliver policies to terminals, eliminating the need to manually configure different policies for each type of service terminals.
Terminal policies can be delivered based on the terminal type, operating system, or vendor.
Enable terminal-type-based automatic policy delivery, so that policies are authorized based on the admission authentication result.
Deploy admission authentication on access switches and APs.
Enable MAC address authentication on access switches and APs when dumb terminals are deployed.
Perform policy design.
Enable the terminal identification function on the network.
Sort out the types of terminals that require automatic policy delivery on the network, design corresponding authorization policies, and configure the policies on iMaster NCE-Campus.
Item | Admission Policy | Authorization Policy
Operating system: Android | User admission | Authorized ACL 1
Operating system: iOS | User admission | Authorized ACL 2
Terminal type: printer | Automatic admission | Authorized VLAN 10
Terminal type: IP camera | Automatic admission | Authorized VLAN 20
Terminal type: IP phone | Automatic admission | Authorized VLAN 30; DSCP 48
Terminal type: access control device | Automatic admission | Authorized VLAN 40
Vendor: ABC | User admission | Authorized ACL 100
1
2
3
User Management
User Authentication
Policy Control
Terminal Identification
Notes: It is recommended that admission and authorization policies be automatically delivered to dumb terminals (such as printers, IP phones, and IP cameras) based on terminal types. This helps implement automatic service provisioning and plug-and-play for dumb terminals.

## Slide 94
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 95: WLAN Service Solution
On a large- or medium-sized campus network, the WLAN typically uses the "AC + Fit AP" networking architecture.
An AC can be deployed in in-path or off-path mode, depending on its location. A native AC (integrated on a switch) must be deployed in in-path mode, whereas a standalone AC can be deployed in either in-path or off-path mode (off-path mode is recommended).
Native AC solution
Switches provide the native AC function.
Free mobility is supported. Policies for wired and wireless users are centrally enforced on the switches.
Unified management of wired and wireless users.
Standalone AC solution
Standalone AC (connected to the core switch in off-path mode).
The free mobility solution is supported for wireless users, but it must be used together with the IP-security group entry synchronization solution.
Separate management for wired and wireless users.
AC
AC
Native AC
Notes: Control packets between an AC and AP are forwarded through a CAPWAP tunnel. APs forward service packets of wireless users to the wired side in tunnel forwarding (centralized forwarding) or direct forwarding (local forwarding) mode.
  Tunnel forwarding:
    Application scenario: Service packets of wireless users are centrally processed and forwarded by the AC.
    Advantages: The AC centrally forwards service traffic, ensuring high security and facilitating centralized traffic management and control.
    Disadvantages: Service packets must be forwarded by the AC, resulting in low forwarding efficiency and a heavy load on the AC.
  Direct forwarding:
    Application scenario: Service packets of wireless users are directly forwarded without passing through the AC, saving link bandwidth between the AP and AC.
    Advantages: Service packets are forwarded without passing through the AC, which is efficient and reduces the load on the AC.
    Disadvantages: Service data is difficult to manage and control in a centralized manner.
  The tunnel forwarding mode is recommended for the native AC solution.

## Slide 96: Native AC Solution Deployment on a VXLAN-based Virtualized Campus Network
Centralized gateway scenario
Scenario 1: The switch used as the border node provides the native AC function to manage network-wide APs.
It is recommended that the native AC function be deployed on the border node and the tunnel forwarding mode be used on APs.
Traffic of wireless users enters into VNs through the native AC, and the border node functions as the gateway of wireless users.
Free mobility is supported, and free mobility policies for wireless user groups are enforced on the border node.
Border
Layer 3 gateway
Edge
Edge
Native AC
CAPWAP tunnel
Distributed gateway scenario
Scenario 2: The switch used as the border node provides the native AC function to manage network-wide APs.
When the number of wireless users on the entire network exceeds 50,000, the distributed gateway solution is recommended. In this scenario, the tunnel forwarding mode is recommended for APs.
Traffic of wireless users enters into VNs through the native AC, and the border node functions as the gateway of wireless users.
Free mobility is supported, and free mobility policies for wireless user groups are enforced on the border node.
Border
Edge
Layer 3 gateway
Edge
Layer 3 gateway
Native AC
CAPWAP tunnel
Notes: Description of the centralized gateway scenario:
  User gateway: border node
  Authentication point: edge node for wired users; border node (native AC) for wireless users
  Forwarding model:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node. The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (native AC).
Description of the distributed gateway scenario:
  User gateway: edge node for wired users; border node for wireless users
  Authentication point: edge node for wired users; border node (native AC) for wireless users
  Forwarding model:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node. The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (native AC).

## Slide 97: Standalone AC Solution Deployment on a VXLAN-based Virtualized Campus Network
Centralized gateway scenario
Border
Layer 3 gateway for wireless users
Edge
Edge
CAPWAP tunnel
Distributed gateway scenario
The AC centrally manages APs. The tunnel forwarding mode is used. Traffic of wireless users is encapsulated by the AP using the CAPWAP protocol and then sent to the AC. After being decapsulated by the AC, the traffic enters the VN through the border node.
The border node functions as the gateway for wireless users.
Free mobility is supported, and free mobility policies for wireless user groups are enforced on the border node.
Standalone AC
Border
Layer 3 gateway for wireless users
Edge
Layer 3 gateway for wired users
Edge
Layer 3 gateway for wired users
CAPWAP tunnel
Standalone AC
The AC centrally manages APs. The tunnel forwarding mode is used. Traffic of wireless users is encapsulated by the AP using the CAPWAP protocol and then sent to the AC. After being decapsulated by the AC, the traffic enters the VN through the border node.
The border node functions as the gateway for wireless users.
Free mobility is supported, and free mobility policies for wireless user groups are enforced on the border node.
Notes: Description of the centralized gateway scenario:
  User gateway: border node
  Authentication point: edge node for wired users; standalone AC for wireless users
  Forwarding model:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: Free mobility policies are enforced on the border node (the border node needs to subscribe to IP-security group entries). The tunnel forwarding mode is recommended. Traffic enters VNs through the border node (traffic is forwarded from the standalone AC to the border node and then enters VNs).
Description of the distributed gateway scenario:
  User gateway: edge node for wired users; border node for wireless users when tunnel forwarding mode is used
  Authentication point: edge node for wired users; AC for wireless users

## Slide 98
Notes:   Forwarding model:
    Wired traffic: Traffic enters VNs through the edge node, and free mobility policies are enforced on the edge node.
    Wireless traffic: The tunnel forwarding mode is recommended. Traffic enters VNs through the border node, and the border node enforces free mobility policies (the border node needs to subscribe to IP-security group entries).
Note: By default, port isolation is configured by the controller on the interfaces for connecting the border nodes to the standalone ACs. Therefore, when standalone ACs work in VRRP-based hot standby mode, a heartbeat link needs to be deployed between the active and standby ACs, and the switch ports connected to the ACs need to be configured to allow packets from the management VLAN of the ACs.

## Slide 99: Deployment of WLAN Deployment Solutions on a VXLAN-based Virtualized Campus Network
The following table lists the recommended WLAN deployment solutions for centralized and distributed gateway networking.
In new deployment scenarios or wired and wireless network reconstruction scenarios, the native AC is recommended and tunnel forwarding mode is preferentially selected for APs.
Networking Type | AC | Gateway for Wireless Terminals | AP Forwarding Mode | Wireless Traffic Virtualization Location | Number of Terminals Supported | Applicable Scenario
Centralized gateway | Native AC on the border node | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the number of terminals does not exceed 50,000 and centralized forwarding is implemented for wireless terminals.
 | Standalone AC connected to the border node in off-path mode | Border node | Tunnel forwarding | Border node | ≤ 50,000 | Recommended when the wired network is reconstructed first and centralized forwarding is implemented for wireless terminals.
Distributed gateway | Native AC on the border node | Border node | Tunnel forwarding | Border node | 50,000~100,000 | Recommended when the number of terminals exceeds 50,000 and centralized forwarding is implemented for wireless terminals.

## Slide 100
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 101: Network Egress Design Overview
As the boundary between a campus network and external networks (including the Internet and WAN), the egress zone is responsible for communication and security protection between internal and external networks.
The requirements for the egress zone design are as follows:
  Network connectivity: Internal users can access external networks. If the campus network provides access for external users, external users should be able to access the internal network.
  Network security: To ensure that the campus network is secure and controllable, especially border security, firewalls and the Intrusion Prevention System (IPS) devices need to be configured. Security components are selected based on security requirements and investment scales.
  Flexible access modes: Various access modes are provided, including LAN-side and WAN-side access.
  Strong service control capability: Service deployment and isolation are easy to implement, and various VPN access modes are provided, including IPsec VPN, SSL VPN, and MPLS VPN.
Core layer
Aggregation layer
Access layer
iStack/CSS link
Terminal layer
DC
O&M zone
Internet
WAN
Egress zone

## Slide 102: Egress Network Service Scenarios (1)
Internet
Egress zone
Security
NAT
Remote access
Multi-campus interconnection
Security
Multi-campus interconnection
WAN
Service Scenario | Sub-scenario | Description | Applicable Network
Security | Firewall | A firewall uses security zones to divide networks and identify packet forwarding paths. When a packet is transmitted between security zones, the firewall can perform a security check and enforce corresponding security policies. | Internet and leased line
 | URL filtering | URL filtering controls internal users' access to external URLs. It allows or forbids users to access certain web page resources, thereby regulating online behaviors. | Internet
NAT | Source NAT | Intranet users usually use private IP addresses to access the Internet. To ensure successful access to Internet services, private IP addresses must be translated into public IP addresses. | Internet
 | NAT server | Servers deployed on the campus network, such as the file server, can be mapped to the Internet using public IP addresses or public IP addresses and port numbers through the NAT server, so that they can be accessed from the Internet. | Internet

## Slide 103: Egress Network Service Scenarios (2)
Internet
Egress zone
Security
NAT
Remote access
Multi-campus interconnection
Security
Multi-campus interconnection
WAN
Service Scenario | Sub-scenario | Description | Applicable Network
Remote access | SSL VPN access | The SSL VPN gateway connects to the Internet and provides SSL VPN services for mobile office users (employees on business trips). After a mobile user uses a terminal (such as a laptop or smart phone) to establish an SSL VPN tunnel with the gateway, the user can remotely access intranet resources such as the web server, file server, and mail server through the SSL VPN tunnel. | Internet
Multi-campus interconnection | Traditional MPLS VPN interconnection | CE devices can be connected to the MPLS VPN network. | Leased line
 | IPsec VPN interconnection | IPsec VPN tunnels are established between multiple campuses to ensure secure data transmission on a low-security bearer network. | Internet and leased line

## Slide 104: WAN-side Connection Design
Internet
WAN
Internet
Internet2
/WAN
Internet1
Optional
WAN
Internet
WAN
Internet
LTE
Single router and single egress
Single router and dual egresses
Dual routers and single egress
Dual routers and dual egresses
Dual routers and multiple egresses
Optional
Optional
Optional
Optional
Router as egress
Firewall as egress
Internet
WAN
Internet
Internet2
/WAN
Internet1
Internet2
/WAN
Internet1
Single firewall and single egress
Single firewall and dual egresses
Dual firewalls and single egress
Dual firewalls and dual egresses
Hot standby heartbeat link
The following factors need to be considered during the WAN-side connection design:
Egress link type
SD-WAN requirements
Protocol interconnection requirements
Must be ARs
Notes: To ensure reliability, routers and firewalls are usually deployed in redundancy mode. It is recommended that devices be deployed in redundancy mode at the egress of a large- or medium-sized campus network.
WAN-side connection design:
  Egress link type
    Ethernet: Select routers (NE or AR series) or firewalls as egress devices.
    For non-Ethernet links, such as EI, CE1, and CPOS links, select routers as egress devices.
  SD-WAN requirements:
    If there are SD-WAN requirements, select AR routers as egress devices.
    If there is no SD-WAN requirement, select firewalls or NE routers as egress devices.
  Protocol interconnection requirements:
    If BGP runs between egress devices and external networks, it is recommended that routers be used as the egress devices. This is because routers have a larger number of routing table entries and higher performance and many routing policies need to be deployed on egress devices.

## Slide 105: LAN-side Connection Design
CSS
A single firewall is connected to a single core switch
Two firewalls are connected to a CSS of core switches in square-looped mode
CSS
A single router is connected to a single core switch
Two routers are connected to a CSS of core switches in square-looped mode
CSS
Two firewalls are connected to a CSS of core switches in dual-homed mode
CSS
Two routers are connected to a CSS of core switches in dual-homed mode
LAN-side connection design
It is recommended that core switches be deployed in cluster or stack mode to form a logical switch, thereby ensuring reliability of core switches.
Egress gateways are usually deployed in a two-node cluster to meet reliability requirements. Different types of gateways differ slightly in their two-node cluster deployment capabilities. For example, the link between the active and standby firewalls in a two-node cluster is used only for heartbeat and entry synchronization, and not for traffic forwarding. The link between routers functioning as gateways can be used for service interconnection and for synchronizing and backing up information between them.
It is recommended that egress gateways and core switches be connected in dual-homed mode and link aggregation be used to enhance the link-level reliability and forwarding bandwidth between devices.
Hot standby heartbeat link
CSS
Link aggregation

## Slide 106: Firewall Hot Standby
When firewalls function as egress devices, you are advised to deploy HSB to improve firewall reliability.
CSS/iStack
Link aggregation
Service packet
Hot standby
Active firewall
Standby firewall
Core switch
Hot standby
Active firewall
fails
Standby firewall
As shown in the figures, the firewalls act as egress devices of the campus network and are directly connected to the core switches. The two firewalls are configured to work in HSB mode, and the Eth-Trunk links connecting the firewalls and core switches work in active/standby mode. When the active firewall is faulty, the standby firewall takes over services from it and forwards service packets.

## Slide 107: Off-Path Deployment of Firewalls
Deploying firewalls in off-path mode
In addition to in-path deployment, firewalls can be deployed in off-path mode. Generally, off-path deployment of firewalls is selected based on the following principles:
  Whether traffic passes through a firewall can be flexibly defined.
  Expansion is easy, for example, in the network reconstruction scenario.
  A firewall fault has little impact on services.
On a campus network:
  If a firewall is used as the egress gateway, the firewall usually provides functions such as security policies, NAT, and VPN gateway. If the north-south traffic must pass through the firewall and if scalability is not considered, in-path deployment is recommended for the firewall.
  If a router is used as the egress gateway and the firewall only provides advanced security functions, such as intrusion prevention, antivirus, and URL filtering, off-path deployment can be used for the firewall.
HSB heartbeat link
CSS/iStack
Link aggregation
Two firewalls connected to the border node in off-path mode
WAN
Internet
OA PC1
OA PC2
RD PC3
Traffic from PC1 to the Internet
Traffic from PC2 to PC3

## Slide 108: Egress Routing Design: In-Path Firewall Deployment
Routes between a firewall and core switch include routes from the campus intranet to external networks on the core switch as well as return routes from external networks to the campus intranet on the firewall.
If a firewall is deployed in in-path mode, you are advised to configure static routes for communication between the core switch and firewall.
FW
Border
Public
VRF1
VRF2
vsys1
vsys2
10.11.0.254 VLANIF11
10.11.0.1 VLANIF11
Virtual-if1
Virtual-if0
Virtual-if2
VLANIF12 10.12.0.254
VLANIF12 10.12.0.1
Internet
GE0/0/1 1.2.3.3
Route design for intranet users to access the Internet
Routes for traffic from Intranet users to the Internet:
Border: default static VPN route, with the next hop being the IP address of the private network interface VLANIF11 of vsys1.
vsys1: default static route, with the next hop being Public, which directs traffic from intranet users to the Internet to the public system.
FW: default static route, with the next hop being the public network gateway address.
Return route:
vsys1: static route, with the next hop being the IP address of the Layer 3 interface corresponding to VRF1 on the border node, which diverts return traffic from the Internet to users in vsys1 to the intranet.
1.2.3.4
Virtual interface
Logical interface
Physical interface
User traffic
Note: In this example, the border node is interconnected with external networks in L3 exclusive egress mode.
Notes: Routes for the traffic from intranet users to the Internet:
  [Border] ip route-static vpn-instance vpn1 0.0.0.0 0 10.11.0.1
  [vsys1] ip route-static 0.0.0.0 0 public
  [FW] ip route-static 0.0.0.0 0 1.2.3.4
Return route:
  [vsys1] ip route-static 10.11.0.0 24 10.11.0.254
  Note: No return route needs to be configured for the return traffic in the public system. After a return packet matches the session table in the public system, the packet is directly forwarded to vsys1 for processing.

## Slide 109: Egress Routing Design: Off-Path Firewall Deployment
Border
VRF1
GE0/0/2 10.2.0.254
GE0/0/2 10.2.0.1
Internet
GE0/0/1 1.2.3.3
1.2.3.4
AR
Public
VRF2
FW
vsys1
Public
vsys2
Virtual-if0
Virtual-if1
Virtual-if2
VLANIF10
VLANIF11
VLANIF12
10.11.0.254
10.11.0.1
10.12.0.254
10.12.0.1
10.10.0.254
10.10.0.1
In the scenario where the firewall is deployed in off-path mode:
  It is recommended that static routes be configured for communication between the core switch and firewall.
  It is recommended that a dynamic routing protocol (OSPF) be configured for communication between the core switch and egress router.
Physical interface: GE0/0/1
Route design for intranet users to access the Internet
Routes for traffic from Intranet users to the Internet:
Border: default static VPN route, with the next hop being the IP address of the private network interface VLANIF11 of vsys1.
vsys1: default static route, with the next hop being Public, which directs traffic from intranet users to the Internet to the public system.
FW: default static route, with the next hop being the address of VLANIF10 on the border node.
Border: Deploy a dynamic routing protocol between the border node and AR to implement interworking and enable access the Internet.
Return routes:
Border: static route, with the next hop being the address of VLANIF10 on the FW.
vsys1: static route, with the next hop being the IP address of the Layer 3 interface corresponding to VRF1 on the border node, which diverts return traffic from the Internet to users in vsys1 to the intranet.
Virtual interface
Logical interface
Physical interface
User traffic
Note: In this example, the border node is interconnected with external networks in L3 exclusive egress mode.
Notes: Routes for the traffic from intranet users to the Internet:
  [Border] ip route-static vpn-instance vpn1 0.0.0.0 0 10.11.0.1
  [vsys1] ip route-static 0.0.0.0 0 public
  [FW] ip route-static 0.0.0.0 0 10.10.0.254
Return routes:
  [Border] ip route-static 10.11.0.0 24 10.10.0.1
  [vsys1] ip route-static 10.11.0.0 24 10.11.0.254
  Note: No return route needs to be configured for the return traffic in the public system. After a return packet matches the session table in the public system, the packet is directly forwarded to vsys1 for processing.

## Slide 110: Security Zone Design
A security zone, also known as a zone, is a collection of networks connected through one or more interfaces, where users have the same security attributes. There are typically three types of security zones: Trust, DMZ, and Untrust.
  The Trust zone is a security zone with a high security level. It is typically used to define the zone where intranet users are located.
  The DMZ is a security zone with a medium security level. It is typically used to define the zone where the servers that need to provide services for external networks are located.
  The Untrust zone is a security zone with a low security level. It is typically used to define insecure networks such as the Internet.
Security zone planning
A campus intranet is considered secure, but is faced with security threats from the outside. Therefore, assign the Internet to the Untrust zone and the campus intranet to the Trust zone. Deploy security devices at the campus network egress to isolate the intranet from the Internet and defend the intranet against external threats. Allocate the data center to the DMZ, and deploy firewalls in the DMZ to isolate traffic between the campus intranet and servers in the data center.
Data center
Trust
Fabric
Untrust
DMZ
Internet
WAN
Notes: On a virtualized campus network, when the user gateways are located inside the fabric, each Layer 3 egress interface for connecting the fabric to an external network corresponds to a Layer 3 logical interface on the firewall. Each logical interface can be bound to a security zone. If the user gateways are located outside a fabric, you need to bind the gateways to security zones based on the security policies of these gateways.
Most security policies are implemented based on security zones. Each security zone identifies a network, and a firewall connects networks. Firewalls use security zones to divide networks and mark the routes of packets. When packets travel between security zones, security check is triggered and corresponding security policies are enforced. Security zones are isolated by default.

## Slide 111: Security Policy Design
After security zones are created on the firewall, these security zones are isolated from each other by default. To enable communication between security zones (for example, the campus intranet accesses the Internet), you need to configure Layer 3 connectivity and security policies on the firewall.
Untrust
Firewall
Security policy 2
Intrusion detection
Antivirus
URL filtering
DMZ
VN2-Trust
VN1-Trust
Internet
DMZ
VN1
VN2
Security policy 1
Intrusion detection
Antivirus
Path for traffic from the Internet to DMZ
Path for traffic from VN1 to VN2
Destination Zone | Traffic Source | Trust Level | Recommended Security Policies
Internet | External users | Untrusted | Intrusion detection, URL filtering, antivirus
 | Employees on the go | Medium | 
WAN | Enterprise branch | Medium | URL filtering, antivirus
Intranet | Enterprise employees | High | URL filtering, antivirus
 | Guests | Low | 
Recommended security policy design for common zones:
Notes: As shown in the figure, after security policies are configured, VNs on the intranet can communicate with each other, and the external networks can access servers in the DMZ. In addition, different security protection policies can be applied to traffic in different security zones.

## Slide 112
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 113: Overall Security Design
Campus network security design principles
  There is no absolutely secure network but only more comprehensive protection measures.
  Security is changing dynamically. Different networks have different security requirements. Therefore, on-demand network security design is the best choice.
  Security is a system issue. Security design is required in all aspects of the network. In addition to egress security, campus networks also need to consider intranet security and security compliance.
Campus network security system
  Egress security
  Intranet security: wired network security and wireless network security
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
Server zone
Egress
security
Intranet security
Network Security
QoS
Notes: On a traditional campus network, the intranet is often considered secure, and threats mainly come from external networks. Firewalls are often deployed to ensure security on campus borders. As security challenges increase, border defense at the egress cannot meet requirements. The security model needs to shift from passive into proactive and the security scope needs to be expanded from external networks to the intranet to solve security problems from the source (terminals), improving enterprise-wide information security level.

## Slide 114: Egress Network Security Design
Network services provided by the campus intranet to external networks, such as the enterprise website access service and email service, may have potential security risks, threatening the security of the campus intranet. It is recommended that the following security services be deployed on the egress firewall of the campus network to protect the network border:
  Assign networks for the employees, server networks, and external networks to different security zones, so as to inspect and protect inter-zone traffic.
  Enable the content security protection functions based on the type of network services provided for external networks by an enterprise. For example, enable antivirus and intrusion prevention for all servers.
  If employees need to access an external network, enable functions such as URL filtering and antivirus to defend against external threats and prevent information leakage, thereby ensuring enterprise network security.
Network Security
QoS
Egress security solution design:
  Dedicated security devices, such as firewalls and intrusion prevention systems, are recommended.
  Routers with the abovementioned security functions can also be used.
Function | Description
Intrusion prevention | Compares traffic against the intrusion prevention signature database to prevent application-layer attacks, such as buffer overflows, Trojan horses, backdoor attacks, and worms.
Antivirus | Inspects files transmitted on the network for viruses to protect intranets from data breaches and system crashes caused by viruses.
URL filtering | Permits or denies access to URLs to control the online behavior of users.
Security protection functions:

## Slide 115: Wired Network Security Design
Security Risk | Protection Measure
Broadcast storm | Enable traffic suppression and storm control.
DHCP attack | Enable DHCP snooping and configure uplink interfaces as trusted interfaces.
Impersonating legitimate users | Enable IP source guard (IPSG) and dynamic ARP inspection (DAI).
Mutual access | Enable port isolation.
CPU attack | Enable CPU attack defense.
Denial of service (DoS) attack | Enable attack source tracing.
 | Enable port attack defense.
 | Enable user-level rate limiting.
Network Security
QoS
Notes: Security measures:
  Enable traffic suppression and storm control.
    Control broadcast, multicast, and unknown unicast packets to prevent broadcast storms. Traffic suppression limits the traffic using the configured threshold, and storm control blocks the traffic by shutting down interfaces.
  Enable DHCP snooping and configure uplink interfaces as trusted interfaces.
    DHCP snooping defends against bogus DHCP server attacks, DHCP server DoS attacks, bogus DHCP packet attacks, and other DHCP attacks. DHCP snooping allows administrators to configure trusted and untrusted interfaces, so DHCP clients can obtain IP addresses from authorized DHCP servers. A trusted interface forwards the DHCP packets it receives, whereas an untrusted interface discards the DHCP ACK packets and DHCP Offer packets received from a DHCP server.
    An interface directly or indirectly connected to the DHCP server trusted by the administrator needs to be configured as a trusted interface, and other interfaces are configured as untrusted interfaces. This ensures that DHCP clients obtain IP addresses only from authorized DHCP servers and prevents bogus DHCP servers from assigning IP addresses to DHCP clients.
  Enable IPSG and DAI.
    IPSG prevents unauthorized hosts from using IP addresses of authorized hosts or specified IP addresses to access or attack the network.

## Slide 116
Notes:     You can configure DAI to defend against man-in-the-middle (MITM) attacks and prevent theft of authorized user information. When a device receives an ARP packet, it matches the source IP address, source MAC address, VLAN ID, and interface number of the ARP packet against binding entries. If a match is found, the device considers the ARP packet valid and allows it to pass through. Otherwise, the device discards the packet.
  Enable port isolation.
    You are advised to configure port isolation on the interfaces connecting an access switch to terminals. This configuration secures user communication and prevents invalid broadcast packets from affecting user services.
  Enable CPU attack defense.
    CPU attack defense limits the rate of packets sent to the CPU so that only a limited number of packets are sent to the CPU within a certain period of time. This ensures that the CPU can properly process services.
    Control Plane Committed Access Rate (CPCAR) is the core of CPU attack defense. CPCAR limits the rate of protocol packets sent to the control plane to ensure security of the control plane.
  Enable attack source tracing.
    Attack source tracing defends against DoS attacks. A device enabled with attack source tracing analyzes packets sent to the CPU, collects statistics on the packets, and allows a user to set a packet rate threshold for the packets. Packets sent at a threshold-crossing rate are considered as attack packets. The device finds the source user address or source interface of the attacker by analyzing the attack packets and generates logs or alarms to alert a network administrator. The network administrator then takes measures to defend against the attack or configure the device to discard packets sent by the attack source.
  Enable port attack defense.
    Port attack defense is an anti-DoS attack method. It defends against attacks based on ports and prevents protocol packets on ports from occupying bandwidth and causing other packets to be discarded.
    By default, port attack defense is enabled on the device for common user protocol packets, such as ARP, ICMP, DHCP, and IGMP packets. If a user attack occurs, the device restricts the attack impact within the port, reducing the impact on other ports.
  Enable user-level rate limiting.
    User-level rate limiting identifies users based on MAC addresses, and rate-limits specified protocol packets, such as ARP, ND, DHCP Request, DHCPv6 Request, IGMP, 802.1X, and HTTPS-SYN packets. If a user undergoes a DoS attack, other users are not affected.
    Host CAR is the core of user-level rate limiting. By default, user-level rate limiting is enabled.

## Slide 117: Overview of Wireless Network Security Design
On a WLAN, service data is transmitted through radio signals. Such open channels are vulnerable to service data interception and tampering during transmission, such as rogue STAs, spoofing APs, and DoS attacks of malicious terminals.
In addition to the security risks of wired networks, wireless networks also face security risks of wireless air interfaces. Therefore, the security risks of wireless networks mainly involve the security of wireless air interfaces.
WLAN security design involves the following:
  Air interface security: identifies and defends against attacks such as rogue APs, rogue STAs, unauthorized ad-hoc networks, and DoS attacks.
  STA access security: ensures the validity and security of STAs' access to the WLAN.
  Service security: protects service data of authorized users from being intercepted by unauthorized users during transmission.
Core layer
Aggregation layer
Access layer
Egress zone
CSS/iStack link
Rogue STA
A rogue STA goes online
STAs access through a rogue AP
Rogue AP
Illegal data theft
Network Security
QoS

## Slide 118: Wireless Network Security Design
Wireless air interface security design:
Security Risk | Defense Measure
Wireless attack and spoofing | WIDS
 | WIPS
 | Attack detection
Unencrypted management frames | Protected management frame (PMF)
Security Risk | Defense Measure
Air interface encryption and access authentication | WPA/WPA2
 | WAPI
Terminal access security | STA blacklist and whitelist
Brute-force cracking | Brute-force attack defense and dynamic blacklist
STA access security design:
Wireless service security design:
  The wired network between APs and ACs also faces common security threats, for example, interception, tampering, and spoofing, on IP networks.
  To improve data transmission security, CAPWAP tunnels between APs and ACs support Datagram Transport Layer Security (DTLS) encryption, including DTLS encryption of CAPWAP tunnels for management packets, DTLS encryption of CAPWAP tunnels for service data packets, encryption of sensitive information, and integrity check.
Network Security
QoS
Notes: Wireless air interface security design:
  The Wireless Intrusion Detection System (WIDS) can detect rogue and interfering APs, bridges, and STAs, as well as ad-hoc devices.
  The Wireless Intrusion Prevention System (WIPS) can disconnect authorized users from rogue APs, disconnect rogue and interfering devices from the WLAN, and contain such devices.
  Attack detection: The WIDS and WIPS can also detect attacks such as flood attacks, weak initialization vector (IV) attacks, spoofing attacks, brute force WPA/WPA2/WAPI pre-shared key (PSK) cracking, and brute force WEP shared key cracking in a timely manner. The two systems then record logs, statistics, and alarms to notify network administrators of such attacks. The WLAN device adds devices that initiate flood attacks and brute force key cracking attacks to the dynamic blacklist and rejects packets from such devices within the aging time of the dynamic blacklist.
  PMF: Management frames on a WLAN are not encrypted, which may cause security problems. The PMF standard is released by the Wi-Fi Alliance based on IEEE 802.11w. It aims to apply security measures defined in WPA2 to unicast and multicast management action frames to improve network trustworthiness.

## Slide 119
Notes: STA access security design:
  Four WLAN security policies are available: Wired Equivalent Privacy (WEP), Wi-Fi Protected Access (WPA), WPA2, and WLAN Authentication and Privacy Infrastructure (WAPI). Each security policy has a series of security mechanisms, including link authentication used to establish a wireless link, user authentication used when users attempt to connect to a wireless network, and data encryption used during service transmission.
    WEP uses a shared key to authenticate users and encrypt service packets. Since the shared key is easy to decipher, the WEP security policy is not recommended due to its low security.
    WLAN devices support the STA blacklist and whitelist function to filter access requests from STAs based on specified rules, allowing authorized STAs to access the WLAN and rejecting unauthorized STAs.
    When a WLAN uses WPA/WPA2-PSK, WAPI-PSK, or WEP-Shared-Key as the security policy, attackers can use the brute force method to decrypt the password. Defense against brute-force key cracking can prolong the time needed to decrypt passwords.
  The STA access security design is to properly plan and design the access policies of STAs, securing and facilitating STA access.
  The following is an example of the STA access authentication policy. The following access authentication modes are recommended on enterprise wireless networks:
    Enterprise employees: WPA/WPA2-802.1X authentication
    Guests: WPA/WPA2-PPSK or Portal authentication
    Dumb terminals: MAC address authentication
  In addition, if users do not need to communicate with each other, it is recommended that user isolation be configured.
Wireless service security design:
  Sensitive information encryption: When sensitive information is transmitted between an AP and an AC, the information can be encrypted to ensure security. Sensitive information includes the FTP user name, FTP password, AP login user name, AP login password, and service configuration key. During inter-AC roaming, the sensitive information encryption function can also be configured to protect data transmitted between ACs.
  Integrity check: When CAPWAP packets are transmitted between an AP and an AC, these packets may be forged or tampered with or attackers may construct malformed packets to launch attacks. Integrity check can protect CAPWAP packets between the AP and AC. If the AP and AC are both located on the intranet, this function does not need to be enabled. It is recommended that this function be enabled when the AP is connected to the AC across the Internet or the ACs are distributed across the Internet.

## Slide 120: QoS Design
In addition to traditional data services such as web, email, and FTP services, large and medium-sized campus networks also transmit services such as video surveillance, video conferencing, voice call, and production scheduling, which have specific requirements on bandwidth, latency, and jitter. For example, video surveillance and video conferencing require high bandwidth, low latency, and low jitter. The voice service does not require high bandwidth, but requires low latency. When congestion occurs, the voice service must be processed first.
Quality of Service (QoS) is designed to provide different levels of service quality during transmission of data flows to meet requirements of different services for performance indicators such as bandwidth, latency, jitter, packet loss ratio, and throughput. A variety of QoS technologies can be used to improve the network service quality, such as priority mapping, traffic policing, traffic shaping, queue scheduling, and congestion avoidance. These technologies enable the network to deliver an optimal user experience with limited resources.
The QoS design process consists of requirement survey and analysis, traffic classification design, and scheduling policy design.
Network Security
QoS

## Slide 121: Requirement Survey and Analysis
Before deploying QoS, you must be familiar with various services as well as the traffic model and QoS requirements of each service. This helps correctly design QoS policies, so that QoS guarantee can be provided for each service.
Content and purpose of QoS requirement survey:
Requirement Type | Key Points of Requirement Survey | Survey Purpose
Current network situations | Traffic models of various services and E2E forwarding paths of each service, including forwarding paths in normal and abnormal conditions. | To determine the location for QoS policy deployment.
 | Bandwidth bottleneck points on the network and interface bandwidth of each bandwidth bottleneck point. | To determine whether to deploy QoS policies or expand the network capacity.
QoS requirements | Control services, multimedia services, and other important services that need special attention. | To understand traffic types and QoS requirements of each traffic type.
 | Characteristics of various types of traffic that can be identified by network devices. For example, check whether voice traffic uses a proprietary protocol such as SIP or H.323, whether traffic is originated from or destined for a specific interface of a specific server, and whether traffic is originated from or destined for a specific host network segment. | 
 | Bandwidth requirements of important services. For example, multimedia services from different vendors at different bit rates require different bandwidths so that the audio or video services can be smoothly transmitted. | 
 | Processing policies for different multimedia applications. For example, some enterprises require that online videos on intranets be guaranteed and work-irrelevant online videos on the Internet not be guaranteed. | 
Network Security
QoS

## Slide 122: Traffic Classification Design (1)
Services carried on a large- or medium-sized campus network include voice, video, and data services as well as network protocol control signaling required for transmitting the service data.
QoS counters of these services include the bandwidth, packet loss rate, latency, and jitter. Bandwidth can be controlled by configuring parameters, but the packet loss rate, latency, and jitter cannot.
Characteristics and QoS requirements of common services:
Service Category | Typical Application or Protocol | Packet Loss Tolerance | Latency Tolerance | Jitter Tolerance
Network protocols | Link-layer loop prevention protocols, routing protocols, multicast group management protocols, and other protocols designed for network connectivity and interoperability. | Low | Low | Allowed
Management protocols | Protocols used by network administrators for monitoring network devices, delivering configurations, and diagnosing faults. | Low | Low | Allowed
VoIP data flow | Real-time voice calls over IP networks. The network must provide low latency and low jitter to ensure service quality. | Very low | Very low | Very low
Voice signaling | Signaling protocols for controlling VoIP calls and establishing communication channels. Signaling protocols have a lower priority than VoIP data flows because intermittent voices are often considered worse than call failure. | Low | Low | Allowed
Multimedia conferencing | Multiple parties share camera feeds and screens over IP networks. In addition, the protocols or applications provide the adaptive bit rate capability. When the network quality is poor, the system automatically decreases the bit rate and image quality to ensure smooth video communication. | Low or medium | Very low | Low
Network Security
QoS
Notes: Service category examples:
  Network protocols: STP, OSPF, IGMP, etc.
  Management protocols: ICMP, SNMP, Telnet, etc.
  Voice signaling: signaling protocols such as SIP, H.323, H.248, and Media Gateway Control Protocol (MGCP).

## Slide 123: Traffic Classification Design (2)
Characteristics and QoS requirements of common services (continued):
Service Category | Typical Application or Protocol | Packet Loss Tolerance | Latency Tolerance | Jitter Tolerance
Gaming | The network is required to provide online interactive applications with a low packet loss rate, low latency, and low jitter to ensure fast and accurate response during gaming. | Low | Very low | Low
Streaming media | Online audio and video streaming. Audio and video programs are made in advance and then cached on local terminals before being played. Therefore, they have lower requirements for network delay, packet loss, and jitter. | Low or medium | Medium | Allowed
Online live telecasting | Unlike streaming media, data of online live telecasting is sent and received in real time. Though terminals provide the cache mechanism, the network is required to provide a low packet loss rate and jitter to meet real-time requirements and ensure good experience. | Very low | Medium | Low
Low-latency data services | Data services for which users are waiting for output. | Low | Low or medium | Allowed
Bandwidth-intensive services | Network services that involve the transmission of a large amount of data for a long period of time. | Low | Medium or high | Allowed
Common services | Basic services that are not so important and have no special requirements on enterprise networks. | No special requirements | No special requirements | No special requirements
Low-priority services | Services that of no concern or importance to enterprises. | High | High | Allowed
Network Security
QoS
Notes: Service category examples:
  Gaming: for example, online games that transmit operation instructions through RTP or UDP, which poses higher requirements on the network.
  Low-latency data services: for example, long delay on an online ordering system may reduce the revenue and efficiency of enterprises.
  Large-volume data services: for example, FTP, database backup, and file dump.
  Common services: for example, mail and web browsing.
  Low-priority services: for example, network applications irrelevant to work, such as social networking and entertaining videos.

## Slide 124: Scheduling Policy Design
The design of traditional QoS scheduling policies covers both wired networks and WLANs. The design for WLANs focuses on policies related to STA services.
Scheduling policy design for wired networks
The basic principle of traditional QoS design for wired networks is to mark or re-mark packets at boundaries of different DiffServ domains and perform bandwidth control.
Devices in the same DiffServ domain only need to schedule packets in queues based on the priorities marked on boundary nodes.
Service deployment typically involves the following:
  Traffic identification at the access layer
  DiffServ deployment at the aggregation or core layer
  Bandwidth control on the egress firewall
Scheduling policy design for WLANs
The network efficiency of WLANs is lower than that of wired networks, and STAs are more sensitive to user experience. Therefore, you are advised to consider the following when designing the QoS policies for STAs:
  User bandwidth
  Channel preemption
  Signal strength of APs to which STAs are associated
  Multicast service experience
  VIP user experience
Network Security
QoS
Notes: Scheduling policy design for wired networks:
  Traffic identification at the access layer: Access switches function as boundary switches. The switches identify, classify, and mark data flows at the user side. In actual deployments, different interfaces on access switches are connected to different terminals, and different priorities can be allocated to different services on the access switches. Then traffic of the services can be scheduled based on the priorities.
  DiffServ deployment at the aggregation or core layer: Interfaces on aggregation and core switches are configured to trust DSCP or 802.1p priorities and enforce QoS policies based on priorities marked at the access layer. This ensures that high-priority services are scheduled first. A switch interface trusts 802.1p priorities by default.
  Bandwidth control on the egress device: Egress devices are also located in the DiffServ domain and are configured to trust DSCP or 802.1p priorities of packets and implement QoS policies. Due to egress bandwidth limits, you need to consider differences when setting bandwidth parameters for WAN interfaces of egress devices. Additionally, QoS policies of egress devices vary according to the enterprise WAN construction mode.

## Slide 125
Notes:     WAN QoS policies can be managed by an enterprise itself in the following scenarios: enterprise-built WAN, private line built using leased fibers, and customized enterprise QoS policies applied to the carrier WAN. In these scenarios, egress or PE devices do not need to re-mark traffic.
    WAN QoS policies are not controlled by an enterprise itself in the following scenarios: The enterprise leases the private line network of a carrier, and the carrier does not trust the packet marking on the enterprise network or the two parties have different definitions for the same packet marking. Thus, egress devices on the campus network need to re-mark traffic.
Scheduling policy design for WLANs:
  The maximum bandwidth of a single user can be limited based on service requirements. If multiple SSIDs are planned, the total bandwidth of non-critical SSIDs can be limited.
  In high-density scenarios, many users preempt channel resources. As a result, the Internet access service of each user deteriorates. You are advised to enable the following functions in these scenarios:
    Call admission control (CAC): This function controls STA access based on the radio channel utilization and the number of online STAs or signal-to-noise ratio (SNR), thereby ensuring the Internet access service quality of online STAs.
    Dynamic adjustment of enhanced distributed channel access (EDCA) parameters: This function allows APs to adjust EDCA parameters flexibly by detecting the number of STAs to reduce the possibility of collision and improve throughput, thereby enhancing user experience.
  To enable STAs (especially sticky STAs) to re-associate with or roam to APs with stronger signals, enable the function of quickly disconnecting STAs to force low-SNR or low-rate STAs to go offline.
  In scenarios that have high requirements on multicast service experience, you are advised to enable the multicast-to-unicast conversion function to prevent low-rate STAs from affecting multicast services, thus improving multicast service experience (for example, HD VoD service).
  In scenarios where VIP user experience needs to be guaranteed, you are advised to enable preferential access of VIP users to ensure preferential access, scheduling, and bandwidth guarantee for VIP users.

## Slide 126: Suggestions on Scheduling Policy Design
The definition of important data services varies with enterprises. For a portal website, Internet access and gaming traffic is important; for the financial industry, real-time transaction is more important than voice services, and Internet access and gaming traffic is unwanted. Therefore, QoS policies must be designed and deployed based on actual service types and QoS requirements of each enterprise.
Recommended scheduling policy design:
Application Type | Typical Application or Protocol | CoS | Queue (Priority) | Scheduling Algorithm | Maximum Bandwidth
Signaling and control | Routing protocols Network management protocols Multimedia protocol signaling | CS6 | 6 | PQ | Unlimited
Real-time interactive multimedia | VoIP Multimedia conferencing Online gaming Desktop cloud | EF | 5 | PQ | Available interface bandwidth x 30%
On-demand subscription of multimedia or key services | Online video Video live telecasting or multicast Delay-sensitive and mission-critical enterprise services that require real-time interaction, such as online ordering | AF | 4 | DRR: with weight being 20 | Unlimited
Other services | Common Internet access services such as email and web browsing | BE | 0 | DRR: with weight being 20 | Unlimited
Network Security
QoS

## Slide 127
CloudCampus Solution and Virtualized Campus Network Overview
Network Architecture Design
Underlay Network Design
Fabric and Overlay Network Design
Admission Control and Free Mobility Design
WLAN Design
Egress Network Design
Network Security and QoS Design
O&M Design

## Slide 128: Challenges Facing Campus Network O&M
Precise detection
Fault identification
Experience perception
During traditional O&M, network faults can be detected only after receiving clients' complaints. As a result, faults cannot be effectively and proactively identified and analyzed.
Traditional O&M is based on SNMP and therefore data collection takes minutes. Once a fault occurs, data generated at the time when the fault occurred cannot be obtained in real time. In addition, no convenient backtracking method is available.
In traditional O&M systems, only device metrics are monitored. User experience may be poor even if the metrics are normal. In addition, traditional O&M systems do not provide correlative analysis for clients and networks.
Key requirements: intelligent fault identification
Key requirements: client & network profiling, experience perception
Key requirements: Telemetry-based precise detection

## Slide 129: Campus Network O&M Panorama
Visualized management and monitoring
Device management
Log management
Alarm management
File/Configuration management
NE management
Service quality monitoring
Link management
Wireless network monitoring
Network management
Terminal management
Customer flow analysis
User management
Terminal management
Device dimension
User roaming dimension
User application dimension
User access dimension
User throughput dimension
Network health
Intelligent troubleshooting
Device diagnosis and test
SLA management
Packet header obtaining
Packet path tracing
Fault locating
Access analysis
Protocol trace
Issue analysis
Performance analysis
Fault analysis
Radio calibration
Network optimization
Controller
Analyzer
CloudCampus
APP

## Slide 130: Basic Network O&M Design
In the large- and medium-sized virtualized campus network solution, iMaster NCE-Campus provides comprehensive basic network management, network element (NE) management, service management, and system management functions for managed devices. These functions include user, log, resource, topology, alarm, and performance management. In addition, protocols involved in traditional network O&M can also be applied on iMaster NCE-Campus.
Protocol Name | Configurations Supported on iMaster NCE-Campus
SNMP | Interconnection between network devices and an SNMP server can be configured on iMaster NCE-Campus. iMaster NCE-Campus can manage traditional devices (NETCONF-incapable devices) using SNMP.
NTP | Interconnection between network devices and an NTP server can be configured on iMaster NCE-Campus.
Syslog | Interconnection between iMaster NCE-Campus and a Syslog server can be configured. After they are interconnected, iMaster NCE-Campus uploads the logs obtained from network devices to the Syslog server. Interconnection between network devices and a Syslog server can be configured on iMaster NCE-Campus.
SSH | Local accounts for SSH-based login can be configured on network devices. SSH can be used to log in to the CLI of a network device from iMaster NCE-Campus.
LLDP | LLDP can be enabled for network devices on iMaster NCE-Campus. LLDP is enabled on iMaster NCE-Campus by default. iMaster NCE-Campus can obtain network topology information through LLDP.

## Slide 131: Intelligent O&M Design
Huawei's intelligent O&M solution uses Telemetry technology to send O&M data (such as device performance indicators and terminal logs) on network devices to Huawei iMaster NCE-CampusInsight. iMaster NCE-CampusInsight then uses big data technology, AI algorithms, and other advanced analysis technologies to digitize user experience on the network, helping customers promptly detect network problems and ultimately improve user experience.
O&M functions provided by iMaster NCE-CampusInsight:
Category | Function
Network visualization | Wireless network health
 | Wired network health
 | Integrated topology
Campus service analysis | Issue analysis
 | Access analysis
 | Performance analysis
 | Protocol tracing
Intelligent wireless network | Intelligent radio calibration
 | WLAN topology
User application experience | Application analysis

## Slide 132: Deployment Design for the Intelligent O&M Solution
The deployment process for Huawei intelligent O&M solution involves the following:
  Interconnection between iMaster NCE-Campus and iMaster NCE-CampusInsight: iMaster NCE-Campus can perform unified O&M and management, and iMaster NCE-CampusInsight can be invoked as a proxy service. iMaster NCE-Campus can synchronize site and device information to iMaster NCE-CampusInsight.
  Collection of data such as syslogs and performance data of network devices: The network devices must be enabled to collect O&M data and report the data to iMaster NCE-CampusInsight.
The intelligent O&M solution consists of iMaster NCE-CampusInsight, iMaster NCE-Campus, and devices. Currently, iMaster NCE-CampusInsight can manage Huawei cloud switches and APs, and intelligently analyzes their data.
Devices need to periodically report data to iMaster NCE-CampusInsight. Therefore, the campus network needs to reserve bandwidth for data reporting. The average bandwidth consumed by each device is 3 kbit/s.
Network bandwidth design
iMaster NCE-CampusInsight and iMaster NCE-Campus can be deployed at different locations. They can collaborate with each other as long as network connectivity is achieved. To avoid instability of the intermediate network, you are advised to deploy them in the same location, for example, a same data center.
Deployment location design

## Slide 133: Precautions for Intelligent O&M Design
During network deployment, ensure that there are reachable routes between network devices and the analyzer iMaster NCE-CampusInsight so that the network devices can send KPI data and log information to iMaster NCE-CampusInsight.
During network deployment, ensure that devices are clock-synchronized with iMaster NCE-CampusInsight. You are advised to deploy an NTP server to synchronize the system clocks on the network.
Network deployment design
To identify DHCP-related connectivity issues and implement protocol trace, you need to use the AC as the DHCP server or enable DHCP snooping on the AC.
Protocol trace function design
The audio and video quality analysis function requires devices to send related log information to iMaster NCE-CampusInsight. You are advised to configure the same log sending interval for switches and WLAN devices. The maximum difference between the log sending intervals cannot exceed 20s.
Audio and video quality analysis function design
Intelligent radio calibration and traditional radio calibration cannot be both deployed on APs in the same region.
Intelligent radio calibration function design

## Slide 134
(Multiple-answer question) For a large-scale campus network with approximately 10,000 terminals, the recommended fabric networking mode is ( ). In this networking mode, the gateway is located on the ( ), and the ( ) functions as the edge node.
  Centralized gateway
  Distributed gateway
  Edge
  Border
  Access switch
  Aggregation switch
Notes: ADF

## Slide 135
To meet requirements of digital transformation, campus networks need to be reconstructed systematically. Based on the IDN concept, Huawei CloudCampus 3.0 Solution helps enterprises build intelligent, simplified, converged, open, and secure networks.
This course focuses on large- and medium-sized campus networks, illustrates the solution architecture and technical solutions used for such networks, and provides suggestions on engineering design and O&M design. With this information, this course helps trainees understand Huawei CloudCampus 3.0 Solution technologies and design the optimal campus network solution.

## Slide 136
Huawei's CloudCampus Solution V100R020C10 Product Documentation
  https://support.huawei.com/hedex/hdx.do?docid=DOC1100797422&lang=en