## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2020.09.28
Zhu Shigeng/00261992
New
Lu Yueyue/WX445705
2021.09.23
Shi Miaomiao/WX791350 & Wu Yue/WX291773
Update

## Slide 2: Virtualized Campus Network Deployment Guide

## Slide 3
Different from traditional campus networks that focus on standalone devices, a virtualized campus network focuses on the overall service experience of the entire network and uses iMaster NCE-Campus and virtual extensible local area network (VXLAN) technology to flexibly schedule network resources. Virtualization technologies group physical network resources into a network-wide resource pool that can be flexibly adjusted by the service layer and allocated by iMaster NCE-Campus. A physical network is virtualized into multiple logically independent virtual networks that carry various services and have independent network resources. This virtualization decouples services from networks and facilitates service management.
This course describes the deployment process and typical deployment cases of the VXLAN-based virtualized campus network solution.

## Slide 4
On completion of this course, you will be able to:
  Describe the deployment process of the CloudCampus VXLAN-based virtualized campus network solution.
  Deploy a typical CloudCampus VXLAN-based virtualized campus network solution.
  Configure iMaster NCE-Campus to manage and maintain the CloudCampus VXLAN-based virtualized campus network.

## Slide 5
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 6: Three Deployment Modes of CloudCampus
Operations entity
Customer
MSP, carrier
Huawei
On-Premise
MSP-owned Cloud
Scenario definition
Target customer
Huawei Public Cloud
Customers purchase and own software entities, such as the controller and analyzer, which can be deployed in their data centers or on the public cloud platform.
MSPs purchase software, such as the controller and analyzer, for operational purposes. The software can be deployed in their data centers or on the public cloud platform.
Huawei operates the public cloud and customers do not need to purchase the controller or analyzer software. Instead, customers just purchase Huawei's cloud managed network service.
Customers in industries such as government, education, large enterprise, retail, and financial services
MSP, carrier
Customers in industries such as government, education, large enterprise, retail, and financial services
Software transaction mode
Perpetual license + SnS
TBL subscription mode
SaaS mode
Notes: Managed service provider (MSP): delivers and manages network-based services, applications, and devices. The serviced objects include enterprises, residential areas, and other service providers.
Perpetual license + SnS: The perpetual license is sold together with SnS services, such as software patches, software upgrades (including new features of new releases), and remote support. In the perpetual license + SnS mode, a customer needs to pay SnS fee for a certain period of time, in addition to purchasing the license upon the first purchase. If the customer does not renew the SnS annual fee after it expires, the customer can only use functions provided in the license for the current version and cannot use the service functions covered in the SnS annual fee.
SaaS mode: MSPs are responsible for deploying or leasing hardware infrastructure, and O&M and management of the hardware and software. Software is provided for customers as cloud services and customers need to periodically pay for the cloud services.
Term Based License (TBL) mode: This mode differs from the perpetual license + SnS mode in that the licenses purchased by customers have limited validity periods. If a customer does not renew the subscription after the license expires, the customer can no longer use the software product.
SnS: refers to Subscription and Support. It consists of two parts: software support and software subscription. The complete software charging mode consists of the annual software SnS fee and software license fee.
Note: This course uses the on-premise deployment as an example.

## Slide 7: Review: Virtualized Campus Network Architecture
Underlay: a physical topology consisting of physical network devices, such as switches, access points (APs), firewalls, and routers, to provide interconnection capabilities for all services on the campus network, building the basic bearer network for campus service data forwarding.
Fabric: a network with pooled resources abstracted from the underlay network. When creating an instantiated virtual network, you can select the pooled network resources on the fabric.
Virtual network: a logically isolated virtual network instance that is constructed by instantiating a fabric. One virtual network corresponds to one isolated network (service network), for example, research network.
Underlay (physical network layer)
Fabric
Core
Aggregation
Aggregation
Access
Access
Border
BGP EVPN
BGP EVPN
External networks
Network service resources
Edge
Edge
Wired access
Wireless access
Overlay (virtual network layer)
Virtual network 1
Virtual network N
VRF+VNI
VRF+VNI
Network egress
IP/VLAN
Access point
Network services
Fabric instantiation
OSPF
VXLAN

## Slide 8: Review: Network Nodes on a Virtualized Campus Network
Egress gateway: is an egress device of the campus network, which can be an AR router or a firewall.
Border node: implements communication between the fabric and external networks. It is typically a core switch.
Edge node: is a fabric edge device that connects user-side devices to the fabric. Data packets from wired users are encapsulated into VXLAN packets on edge nodes.
Transparent node: is a transparent device on the fabric, and does not need to support VXLAN.
Access node: is typically an access switch (wired access node) or an AP (wireless access node). Wired access nodes can be combined with edge nodes, that is, VXLAN is deployed to the access layer. If wired access nodes do not need to support VXLAN, aggregation nodes can be combined with edge nodes, that is, VXLAN is deployed to the aggregation layer, and policy association is deployed on wired access nodes and VXLAN edge nodes.
Fabric domain (VXLAN)
Access domain
VXLAN-capable nodes
Border node
Transparent node
Edge node
Access node
Egress gateway
Notes: On a fabric, VXLAN tunnel endpoints (VTEPs) are further divided into the following roles:
  Border: is a physical network device and provides data forwarding between the fabric and external networks. In most cases, VXLAN-capable core switches function as border nodes.
  Edge: is a physical network device. Access user traffic enters the fabric from an edge node. Generally, VXLAN-capable access or aggregation switches function as edge nodes.

## Slide 9: Lab: Requirements
To implement multi-service convergence on a campus network, virtual networks are deployed and configured on the campus network through iMaster NCE-Campus. This enables different virtual networks on the same physical network to be divided based on services.
Using the VXLAN technology, virtual networks meet the following requirements:
  Network devices support DHCP-based plug-and-play provisioning.
  Multiple services on the campus network share the same physical network, but are logically isolated. Mutual access control can be implemented among these services.
  Service configuration is automated, and virtual network configurations are delivered by iMaster NCE-Campus, removing the need to log in to devices to manually configure them.
  Users can access virtual networks from anywhere on the campus network, implementing flexible user authentication, onboarding, and free mobility.
HQ
AR3
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
GE0/0/1
ACC_2
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/1
GE0/0/1

## Slide 10: Lab: Gateway Solution Selection
When designing the virtualized campus network solution, first determine the gateway solution to be used. After the gateway solution is determined, you can perform end-to-end design on the entire campus network based on the selected gateway solution.
Item | Centralized Gateway | Distributed Gateway
User gateway location | Border | Edge
O&M deployment | A border node functions as the gateway of all users, and the native AC function is typically enabled on the border node to support wireless services, simplifying O&M deployment. | Multiple edge nodes function as user gateways. This ensures that only part of the network is affected upon the failure of one gateway and facilitates network expansion. The native AC function is enabled on the border node to support wireless services. The O&M deployment is complex.
Terminal scale | ≤ 50,000 (This solution is recommended if the number of terminals does not exceed 50,000.) | 50,000 to 100,000 (This solution is recommended when the number of terminals exceeds 50,000.)

## Slide 11: Lab: Physical and VXLAN Networking
HQ: ACC_1 and ACC_2 function as access devices that connect to wired terminals and provide network services for wired users. AP1 is connected to ACC_2 to provide network services for wireless users. Edge_1 and Edge_2 serve as aggregation devices, and the Border functions as the core device. AR3 works as both the campus egress and the DHCP server, which allocates IP addresses to other devices and user terminals at the HQ. OSPF is used for communication on the underlay network at the HQ.
Cloud: AR_Server_SW is used to simulate the cloud. It connects the HQ and iMaster NCE-Campus, and also functions as the gateway of iMaster NCE-Campus.
VXLAN network (fabric): The network topology for this lab uses a distributed gateway model, in which VXLAN is deployed across core and aggregation layers. Edge_1 and Edge_2 function as the edge nodes of the VXLAN network, whereas Border functions as the border node of the VXLAN network.
HQ
AR3
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
GE0/0/1
GE0/0/9
VXLAN
ACC_2
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/1
GE0/0/1
GE0/0/3
GE0/0/24
AR_Server_SW
Notes: Note: In this lab, the native AC is deployed on the border node to manage APs. The border node also serves as the DHCP server to allocate IP addresses to APs.

## Slide 12: Lab: Virtual Network
Virtual network (VN): Two virtual networks are defined for access of different end users.
  OA VN: for access of sales personnel (Sales_Wired and Sales_Wireless security groups) and marketing personnel (Market_Wired and Market_Wireless security groups)
  RD VN: for access of R&D personnel (RD security group)
External network: Two external networks are defined for the two virtual networks, so different end users can access different external networks.
  OA external network: accessible to sales and marketing personnel.
  RD external network: accessible to R&D personnel.
Network service resource: One network service resource named DHCP_Email is defined to function as both a DHCP server and an email server. It allocates IP addresses to all end users in the two virtual networks.
HQ
AR3
Border
Edge_1
Edge_2
AP1
PC1
PC2
PC3
GE0/0/1
GE0/0/1
GE0/0/23
OA
(Internet)
RD
(Internet)
External networks
DHCP_Email
(DHCP/Other)
Network service resource
OA VN
RD VN
ACC_1
ACC_2
GE0/0/24

## Slide 13: Lab: Security Group and Policy Control Matrix
Security group: Five security groups are defined to identify different end users.
Sales_Wired and Sales_Wireless: security groups to which sales personnel are assigned after they pass 802.1X or Portal authentication.
Market_Wired and Market_Wireless: security groups to which marketing personnel are assigned after they pass 802.1X or Portal authentication.
RD: security group to which R&D personnel are assigned after they pass 802.1X authentication.
Resource group: One resource group is defined, indicating the email server.
RD_VN
Fabric
RD
(802.1X)
OA_VN
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Sales_Wired
RD
security group
Security group-based policy control matrix
Destination Group Source Group | Sales_Wired | Sales_Wireless | Market_Wired | Market_Wireless | RD | E_mail
Sales_Wired |  |  | Deny | Deny | Deny | 
Sales_Wireless |  |  | Deny | Deny | Deny | 
Market_Wired | Deny | Deny |  |  |  | 
Market_Wireless | Deny | Deny |  |  | Deny | 
RD | Deny | Deny |  | Deny |  | Deny
Sales_
Wireless
Market_
Wired
Market_
Wireless
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
Policy control matrix:
Notes: Policy Control Matrix:
  Sales personnel and marketing personnel cannot communicate with each other. Only marketing personnel using wired terminals and R&D personnel can communicate with each other.
  R&D personnel cannot access the E_mail resource group.
  In the policy control matrix, only the communication that is allowed should be permitted and other communication should be denied.

## Slide 14
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 15: Virtualized Campus Network Deployment Flowchart
Start
Server and software installation
License activation
Site creation
Basic network configurations
Network service configurations
End
Install servers.
Connect cables.
Power on servers.
Install iMaster NCE-Campus.
Obtain the ESN of iMaster NCE-Campus.
Obtain licenses of iMaster NCE-Campus.
Load licenses.
Create an administrator.
Create sites.
Add devices, stacks, or AC groups.
Configure device management.
Configure physical links.
Configure network resources.
Configure a fabric.
Configure virtual networks.
Configure the WLAN.
Configure the egress network.
Configure access control.
Configure security services.
Configure QoS.
Configure O&M management.
Network device installation
Install network devices.
Connect cables.
Power on devices.
Configure the underlay network.
Notes: VXLAN-based large- and medium-sized virtualized campus networks have complex services. Therefore, the deployment process is complex. The deployment process provided in this slide is the general process for you reference.
The following part of this course focuses on key operations in the deployment process.

## Slide 16
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 17: Installing Servers and Software (1)
Installing iMaster NCE-Campus
Installing iMaster NCE-CampusInsight
iMaster NCE-Campus can be deployed in the on-premises scenario, Huawei public cloud scenario, and MSP-owned cloud scenario.
Large- and medium-sized campuses typically adopt the on-premises deployment mode, in which enterprises install iMaster NCE-Campus by themselves.
For more information, see iMaster NCE-Campus Product Documentation.
iMaster NCE-CampusInsight can be deployed independently or integrated with iMaster NCE-Campus.
It is recommended that iMaster NCE-CampusInsight be integrated with iMaster NCE-Campus in the CloudCampus Solution.
For more information, see iMaster NCE-CampusInsight Product Documentation.

## Slide 18: Installing Servers and Software (2)
Installing the CloudCampus APP
When installing APs, upload information about their actual installation locations to iMaster NCE-Campus for efficient O&M and value-added services based on terminal locations. The CloudCampus APP can record and upload AP information.
In addition to the deployment function, the CloudCampus APP also provides the Wi-Fi experience testing, speed testing, and video testing.
The CloudCampus APP can be obtained in either of the following methods:
Android system: Search for CloudCampus on Huawei AppGallery and install the CloudCampus APP.
Scan the QR code to download the CloudCampus APP.
Huawei AppGallery

## Slide 19: Preconfiguring Devices
Task | Preconfiguration Plan
Preconfigure AR3. | Complete basic configurations such as assigning VLANs, creating VLANIF interfaces, and configuring IP routing. Configure the DHCP server for plug-and-play of devices at the site. Configure the DHCP server for end user access. Simulate the OA and RD external networks.
HQ
AR3
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
GE0/0/1
GE0/0/9
VXLAN
ACC_2
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/23
GE0/0/24
GE0/0/1
GE0/0/24
GE0/0/24
GE0/0/1
GE0/0/1
GE0/0/3
GE0/0/24
AR_Server_SW

## Slide 20
VXLAN-based Virtualized Campus Network Deployment Plan
VXLAN-based Virtualized Campus Network Deployment Process and Guide
  Deployment Process
  Preparations for Deployment
  Deployment Guide

## Slide 21: Creating Sites and Adding Devices
HQ
Border
Edge_1
ACC_1
AP1
PC1
PC2
PC3
VXLAN
ACC_2
Edge_2
To enable network devices within the same management scope to be centrally managed on iMaster NCE-Campus, you can create a site on iMaster NCE-Campus and add these network devices to the site.
You can add devices when creating a site or after a site is created.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 22: How to Create Sites and Add Devices
Creating sites one by one
Creating sites in a batch
Add devices manually.
1
Download a template (an Excel file) from iMaster NCE-Campus.
2
Fill in the template with site and device information.
3
Import the template to iMaster NCE-Campus.
Site Name | Campus Device Type | Device role | Device Model | Device Type | Device ESN | Device Name
HQ | LSW, AC | CORE | S5731-H24P4XC | LSW | … | Border
HQ | LSW, AC | AGG | S5731-H24P4XC | LSW | .. | Edge_1
… | … | … | … | … | … | …
… | … | … | … | … | … | …
Create sites and import devices in a batch.
Create sites one by one.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: When creating sites, pay attention to the following points:
  To facilitate device management and improve service deployment efficiency, add devices on the same network of a tenant to the same site.
  You can create sites on iMaster NCE-Campus for unified O&M management. Two methods are available to create sites:
    Create sites one by one: You can create sites one by one when a small number of sites need to be added.
    Create sites in a batch: You can create sites in a batch when a large number of sites need to be added.
When adding devices, pay attention to the following points:
  On a VXLAN-based virtualized campus network, managed devices are typically LSWs (switches) and ACs (wireless access controllers).
  To add devices manually, select By Model or By ESN.
  On large- and medium-sized virtualized campus networks, the WLAN typically adopts the architecture of "AC + Fit AP". In this architecture, Fit APs are centrally managed and configured by the native AC. After the native AC is managed by iMaster NCE-Campus, you can be redirected from iMaster NCE-Campus to the web platform of the native AC to manage Fit APs.

## Slide 23: Lab: Creating a Site, Adding Devices, and Configuring the Plug-and-Play Function
Site creation and device addition
  On iMaster NCE-Campus, create a single site to create the HQ site.
  Add devices (Border, Edge_1, Edge_2, ACC_1, ACC_2, and AP1) one by one based on the device model or ESN.
Device plug-and-play (onsite operation)
  Connect and power on the switches and APs on the network.
  The switches obtain IP addresses and iMaster NCE-Campus address/port through AR3, and initiate registration requests to iMaster NCE-Campus. They are managed by iMaster NCE-Campus once registered.
Device management (by iMaster NCE-Campus)
  Check the device registration status.
  Check the physical network topology.
DHCP Offer
Devices proactively register with iMaster NCE-Campus.
1
2
HQ
AR3
（DHCP Server）
Border
Edge_1
ACC_1
AP1
ACC_2
2
1
Devices to be managed by iMaster NCE-Campus
Edge_2
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Device plug-and-play:
  Customer pain points: In traditional network deployment, engineers need to commission network devices one by one onsite, resulting in heavy configuration workload and low efficiency.
  Solution:
    This lab demonstrates the plug-and-play function of network devices in the CloudCampus Solution. The DHCP Option solution is used to implement plug-and-play of switches. In this example, the DHCP service and related parameters must be preconfigured on AR3.
    In this step, switches on the campus network can be directly deployed using factory settings and get managed by iMaster NCE-Campus, greatly reducing the configuration workload.

## Slide 24: Configuring Resource Pools: Global Resource Pool for the Fabric
Before creating a fabric, plan a global resource pool for the fabric, which contains VLAN, bridge domain (BD), VXLAN network identifier (VNI) resources.
Task | Resource Pool Plan
Configure a global resource pool for the fabric. | Configure VLAN resources, including service VLANs (access VLANs for end users) used during virtual network creation, VLANs whose packets are transparently transmitted between the access and aggregation devices, interconnection VLANs used when external networks and network service resources are created for the fabric, and management VLAN for policy association. Configure BDs and VNIs for Layer 2 broadcast domain isolation in virtual networks.
External network
Network service
resources
Border
Edge_1
ACC_1
ACC2
VLAN
VLAN
BD/VNI
VXLAN tunnel
VLAN
VLAN
Edge_2
HQ
VLAN
VLAN
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 25: Lab: Configuring a Fabric Global Resource Pool
Choose Fabric Network > Network Plan. On the resource pool configuration page that is displayed, click Fabric Global Resource Pool, set parameters, and click +.
iMaster NCE-Campus provides the logical topology view to help users understand the meanings of parameters.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Parameters in the fabric global resource pool:
  VLAN: Configure a service VLAN pool when you need to configure VLANs for connecting to external networks, VLANs for connecting to network service resources, CAPWAP management VLAN, and terminal access VLANs.
  Bridge Domain (BD): On a VXLAN network, VNIs can be mapped to BDs in 1:1 mode so that a BD can function as a VXLAN network entity to transmit traffic. A BD is a Layer 2 broadcast domain used to forward data packets on a VXLAN network.
  VXLAN Network Identifier (VNI): A VNI is similar to a VLAN ID and identifies a VXLAN.

## Slide 26: Configuring Resource Pools: Underlay Automation Resource Pool
The underlay automation resource pool defines the interconnection VLANs, interconnection IP addresses, and loopback interface IP addresses used for routing domain orchestration on the underlay network.
Border
Edge_1
ACC_1
ACC_2
Edge_2
HQ
OSPF
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection IP address
Interconnection VLAN
Interconnection VLAN
Task | Resource Pool Plan
Configuring an underlay automation resource pool. | Configure interconnection VLANs, which cannot conflict with the fabric global resource pool and service VLANs for user access. Configure interconnection IP addresses, which cannot conflict with the fabric global resource pool and service IP addresses for user access. Configure loopback interface IP addresses. As the VXLAN control plane uses BGP EVPN, loopback interface IP addresses are required for establishing BGP EVPN peer relationships between border and edge nodes. The preceding resources are used for automatic orchestration of routing domains on the underlay network.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 27: Lab: Configuring an Underlay Automation Resource Pool
On iMaster NCE-Campus, choose Fabric Network > Network Plan. On the resource pool configuration page that is displayed, click Underlay Automation Resource Pool, set related parameters, and click +.
iMaster NCE-Campus provides the logical topology view to help users understand the meanings of parameters.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Parameters for configuring the underlay automation resource pool:
  Interconnection VLAN: Configure an interconnection VLAN pool when border and edge nodes on a fabric need to communicate on the underlay network.
  Interworking IP address: Configure an interconnection IP address pool when border and edge nodes on a fabric need to communicate on the underlay network.
  Loopback interface IP: If automatic routing domain configuration is required on a fabric, configure an IP address pool for the loopback interfaces.

## Slide 28: Configuring Policy Template Resources: User Access Authentication
In the large- and medium-sized virtualized campus network solution, you need to specify the authentication templates to be bound to wired and wireless access points during fabric access management. The authentication templates need to be planned.
The policy template resources configured on iMaster NCE-Campus typically include the RADIUS server template, Portal server template, and user authentication template.
Border
Edge_1
ACC_1
ACC_2
Edge_2
HQ
Controller built-in server
RADIUS server & Portal server
AP1
Authentication point
RD
(802.1X)
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
Wired traffic
Wireless traffic
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 29: Lab: Configuring User Authentication Templates
On iMaster NCE-Campus, choose Fabric Network > Network Planning > Policy Template, and create and configure a RADIUS server template, a Portal server template, and user authentication templates.
Task | Procedure
Create a RADIUS server template. | Select a RADIUS server type. The iMaster NCE-Campus built-in RADIUS server is recommended. Configure the RADIUS server IP address. If the iMaster NCE-Campus built-in RADIUS server is used, you do not need to configure the RADIUS server IP address.
Create a Portal server template. | Select a Portal server type. The iMaster NCE-Campus built-in Portal server is recommended. Configure the Portal server IP address. If the iMaster NCE-Campus built-in Portal server is used, you do not need to configure the Portal server IP address. Configure the Portal server URL. If the iMaster NCE-Campus built-in Portal server is used, you do not need to configure the Portal server URL.
Create user authentication templates. | Select a user authentication mode, which is typically 802.1X authentication, MAC address authentication, or Portal authentication. A template can contain multiple authentication modes. Select the RADIUS server template or Portal server template to be bound.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 30: Configuring a Fabric
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
A fabric is a virtual network built on top of a physical network using the VXLAN technology, and has all resources pooled.
External network
Network service
resources
Task | Procedure
Configure a fabric. | Create a fabric and complete automatic deployment of an underlay network. Create an external network, that is, configure the connectivity between the fabric and external networks (including the interconnection port, interconnection VLAN, interconnection IP address, peer address, and route). Configure network service resources, that is, configure the connectivity between the fabric and network service resources (DHCP server, RADIUS server, Portal server, and other servers). The connectivity configuration includes the device IP address, interconnection VLAN, interconnection IP address, peer IP address, and interconnection port. Configure access management, that is, configure an interface on an access device to invoke an authentication template.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 31: Configuring a Fabric: Creating a Fabric
You need to create a fabric and then complete basic networking configurations for the fabric, including selecting border and edge nodes as well as configuring BGP EVPN of the VXLAN control plane.
In addition, you need to enable automatic routing domain configuration of the underlay network when creating a fabric.
Task | Procedure
Create a fabric. | Select a networking type: centralized or distributed gateway. Select the WAC location: edge node, border node, standalone WAC, or None. Enable the automatic routing domain configuration function of the underlay network. Configure an AS number, that is, configure BGP EVPN and set an RR cluster ID. (Optional) Configure storm suppression on the fabric. To mitigate the risks caused by network storms, you are advised to enable storm suppression. (Optional) Enable the function of reporting terminal identification information. You need to enable this function when the terminal identification function is configured. Add devices to the fabric and specify the devices as border and edge nodes. If VXLAN is deployed across core and aggregation layers on the fabric, you need to configure access switches as extended nodes.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 32: Lab: Creating a Fabric (1)
Define the networking type.
Specify the WAC location.
Create a fabric on the iMaster NCE-Campus GUI and set the networking type.
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
Enable automatic routing domain configuration and automatically deploy BGP EVPN.
Distributed gateway networking with VXLAN deployed across core and aggregation layers
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: A fabric consists of core, aggregation, and access devices. An access device supports access of different network services, reducing costs while improving network device utilization.
A virtualized campus network uses the overlay virtualization technology (VXLAN) to create multiple virtual networks on the same fabric and allow flexible service deployment.
The networking type specifies the network deployment mode of a fabric:
  Centralized: The fabric uses a centralized gateway, which transmits traffic accessing external networks and the intranet. In this networking mode, only the border node can function as the centralized gateway.
  Distributed: The fabric uses distributed gateways. Traffic accessing external networks and the intranet passes through different gateways. In this networking mode, both border nodes and edge nodes can function as gateways.
iMaster NCE-Campus allows you to specify a BGP route reflector (RR) and automatically deploy BGP EVPN configurations on all edge nodes in a fabric.
  AS number: specifies the BGP AS number used in a fabric.
  RR cluster ID: specifies the cluster ID of an RR. If there are multiple RRs in a fabric, for example, if two RRs are configured on a dual-border network, you need to configure a cluster ID for the RRs to prevent BGP routing loops. The value is an integer ranging from 1 to 4294967295 or an IPv4 address.

## Slide 33: Lab: Creating a Fabric (2)
Add devices to the fabric and specify device roles.
Specify the roles of the devices in the fabric.
Distributed gateway networking with VXLAN deployed across core and aggregation layers
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Role: specifies the role of a device in the fabric, including the border node, edge node, and extended node. By default, the role of a device is an extended node.
Route reflector: In a fabric, border devices are typically used as route reflectors, which simplify full-mesh connections required by IBGP and reduce network and CPU loads.

## Slide 34: Lab: Creating a Fabric (3)
Complete automatic deployment of the underlay network on iMaster NCE-Campus.
Enable automatic routing domain configuration.
Define OSPF areas and packet authentication.
Configuring a single OSPF area
Border
Edge_1
ACC_1
ACC_2
Edge_2
HQ
AP1
OSPF
Area 0
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Automatic routing domain configuration: After this function is enabled, the underlay network is automatically configured. You can specify sites for automatic routing domain configuration and specify OSPF route parameters. Currently, the following parameters are supported:
  Domain: In single-domain mode, all devices belong to area 0. In multi-domain mode, all edge nodes are located in their respective non-backbone areas, and border nodes are interconnected through the backbone area (area 0).
  Network type: You can specify the OSPF network type to broadcast, P2MP, or P2P.
  Encryption: You can set the encryption mode between adjacent devices to HMAC-SHA256, MD5, or None.
  Key: It refers to the authentication key ID used for ciphertext authentication on an interface, and must be consistent with that of the peer device. The value is an integer in the range from 1 to 255.
  Password: It specifies the ciphertext authentication key. The value is a string of 1 to 255 characters and cannot contain spaces.
  Confirm password: You need to enter the ciphertext authentication key again for confirmation.
  OSPF graceful: You can enable OSPF GR.

## Slide 35: Lab: Creating a Fabric (4)
Border
Edge_1
ACC_1
ACC_2
BGP EVPN
Edge_2
HQ
AP1
After this step is complete, a fabric is successfully created based on the physical network, and the underlay network configuration (such as interconnection between network devices and OSPF configuration) is automatically completed on iMaster NCE-Campus, laying a foundation for creating virtual networks.
Configure BGP EVPN on iMaster NCE-Campus.
Define BGP EVPN parameters.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: After a fabric is created, the underlay network can be automatically deployed, and configurations such as VLANIF interfaces, loopback interfaces, VTEP IP addresses, and routes required for establishing a BGP EVPN can be automatically provisioned. iMaster NCE-Campus allocates resources from the fabric global resource pool and underlay automation resource pool to devices.

## Slide 36: Configuring a Fabric: Creating an External Network
In the fabric resource model design, external networks are created on border nodes so that terminals on the campus network can access external networks such as the Internet.
Three types of external network resources are defined: Layer 3 shared egress, Layer 3 exclusive egress, and Layer 2 shared egress. If the user gateway is located in the fabric, the Layer 3 shared egress or Layer 3 exclusive egress is used.
  Layer 3 shared egress: Multiple virtual networks on the fabric share a Layer 3 egress to communicate with the egress device. The Layer 3 shared egress helps save interconnection VLAN and IP resources and applies to scenarios where there are low requirements on security control policies between virtual networks.
  Layer 3 exclusive egress: Each virtual network on the fabric exclusively uses a Layer 3 egress to communicate with the egress device. In this case, multiple security zones are typically configured on the firewall, each corresponding to one Layer 3 exclusive egress. The traffic of different virtual networks to the firewall is isolated from each other.
Task | Procedure
Create an external network. | Select the type of the connection with the external network. Select an external network resource type. Configure interconnection physical interfaces, VLANs, and IP addresses. Configure a routing protocol for interconnection.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 37: Lab: Creating an External Network (1)
Create an external network for the fabric and select the egress connection mode.
External network
Network service
resources
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 38: Lab: Creating an External Network (2)
Define the external route to the external network.
Complete basic configurations of the external network, including specifying the external network name, determining whether to connect the external network to the Internet (whether to use the default route as the external route), and configuring the external route.
External network
Network service
resources
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Basic information:
  If Internet connection is enabled, iMaster NCE-Campus uses a default route to direct traffic to the corresponding external network. If Internet connection is disabled, you need to specify a route prefix.

## Slide 39: Lab: Creating an External Network (3)
Configure interconnection information for the external network.
Configure routing information for the external network.
External network
Network service
resources
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
External route
Port
Local IP address
VLAN
Peer IP address
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Interconnection information:
  Select the border device to be connected to the external network, and select the interconnection interface, interconnection IP address, and interconnection VLAN.
  Note: The configured interconnection IP address cannot conflict with IP addresses in the underlay automation resource pool. The configured interconnection VLAN belongs to the global resource pool of the fabric.
Routing information:
  After you click Apply, iMaster NCE-Campus creates a static route to the external network for the border device. (The static route is delivered to the border device only when the external network is invoked by the virtual network.)

## Slide 40: Configuring a Fabric: Creating Network Service Resources
In the fabric resource model design, network service resources are created on a border node so that service terminals on the campus network can access service resources, such as the DHCP server and NAC server, in the network management zone.
You can create multiple network service resources or add IP addresses for accessing multiple network service resources to a network service resource model.
If only a few service resources in the network management zone need to be accessed, you are advised to plan these resources in the same network service resource model. This saves interconnection VLANs and IP addresses and simplifies routing configuration in the network management zone.
Task | Procedure
Create network service resources. | Select a server type, which can be DHCP server, third-party RADIUS server, and third-party Portal server. Configure the IP addresses for accessing network service resources, such as the DHCP service address and iMaster NCE-Campus southbound IP address. Select an interconnection scenario, which can be directly connected to a server or directly connected to a switch. Configure interconnection physical interfaces, VLANs, and IP addresses.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 41: Lab: Creating Network Service Resources (1)
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
Create a network service resource for the fabric and configure the server, including defining the name, type, and IP address of the connected server.
Define the server type.
Define the server IP address.
Define the device IP address segment for interconnection with the server.
External network
Network service resources
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Server configuration:
  Server type: server resource specified by the network service resource. In this example, the defined network service resource are a DHCP server and a E-mail server.
  DHCP server: IPv4 and/or IPv6 address of a DHCP server.
  Server interconnection address pool: If an IPv6 address pool is configured for the DHCP server, this parameter is mandatory. If only an IPv4 address pool is configured for the DHCP server, this parameter is optional.

## Slide 42: Lab: Creating Network Service Resources (2)
Complete device configurations, including selecting the scenario and configuring interconnection information.
Select an interconnection scenario.
Configure interconnection information.
Border
Edge_1
ACC_1
ACC_2
Fabric
Edge_2
HQ
AP1
External network
Network service resources
Interconnection port
Interconnection VLAN
Interconnection IP address
Peer IP address
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Device configuration:
  If Directly connected to a switch is selected, the border node adds the interconnection port to the interconnection VLAN in tagged mode to connect to network resources. If Directly connected to a server is selected, the switch adds the interconnection port to the interconnection VLAN in untagged mode.
  Interconnection device: Select the border node (Border). The device functions as a border node that connects the fabric to the external network service resource.
  Interconnection port: Select the port used by the border node to connect to the network service resource.
  Interconnection VLAN: Select the VLAN used by the border node to connect to the network service resource.
  Interconnection IPv4 address: Select the IP address of the port used by the border node to connect to the network service resource.
  Peer IPv4 address: Select the IP address of the peer device.
  Mask: Select the network mask.
Note: The configured interconnection IP address cannot conflict with the IP address in the underlay automation resource pool. The configured interconnection VLAN belongs to the fabric global resource pool.

## Slide 43: Configuring a Fabric: Configuring Access Management
Access control needs to be deployed on the campus network to authenticate access users, including 802.1X authentication, MAC address authentication, and Portal authentication. The implementation of 802.1X authentication and MAC address authentication requires the use of the RADIUS server, whereas the implementation of Portal authentication requires the use of the RADIUS server and Portal server.
Configuring access management for the fabric is to configure authentication control points and plan access point resources, which will be used during virtual network creation.
Wired access point resources refer to switch interfaces connected to terminals, and wireless access point resources refer to SSIDs connected to terminals.
  During access management configuration for the fabric, three connection types are defined for access ports of switches:
    Extended AP: Huawei Fit APs, which can be managed by iMaster NCE-Campus.
    Extended access switch: Huawei switches, which can be managed by iMaster NCE-Campus.
    Terminal (PCs, phones, dumb terminals, and non-fabric extended access switches or APs): user terminals, switches and APs that cannot be managed by iMaster NCE-Campus, and switches that can be managed by iMaster NCE-Campus but do not support fabric extension.
Access management configuration for the fabric varies depending on the gateway solution.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 44: Lab: Configuring Fabric Access Management (1)
Border
Edge_1
ACC_1
Fabric
Edge_2
HQ
AP1
Authentication control point
Configure access management on Edge_1 and activate authentication on the switch interface.
Policy association
ACC_2
Authentication enforcement point
Configure an authentication enforcement point.
Configure an authentication control point.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Policy association:
  Configure the management VLAN and management IP address for policy association.
  The configured management IP address cannot conflict with the IP addresses in the underlay automation resource pool. The configured management VLAN belongs to the global resource pool of the fabric.

## Slide 45: Lab: Configuring Fabric Access Management (2)
Configure access management on Edge_2 and activate authentication on the switch interface.
Configure an authentication control point.
Border
Edge_1
ACC_1
Fabric
Edge_2
HQ
AP1
ACC_2
Configure an authentication enforcement point.
Authentication control point
Policy association
Authentication enforcement point
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 46: Logical Network
After a fabric is created, you can select network resources in the fabric to create virtual network instances.
To enable access users in different virtual networks to communicate with each other, you need to configure virtual network interworking.
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
OA VN
RD VN
Task | Procedure
Logical network | Create virtual networks. Different virtual networks represent services of different users and can be used to isolate services of these users. Configure virtual network interworking to ensure that there are reachable underlay network routes between users in different virtual networks.
External network
Network service
resources
VN | Access User
OA | Sales_Wired: 172.17.10.0/24 Sales_Wireless: 172.17.11.0/24 Market_Wired: 172.17.20.0/24 Market_Wireless: 172.17.21.0/24
RD | RD: 172.17.30.0/24
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 47: Fabric Resource Pools and Resource Invoking During Virtual Network Creation
Fabric Resource Pool | How to Invoke Resources in the Resource Pool During Virtual Network Creation
VLAN resource pool, which is used in scenarios where terminals are connected to virtual networks and virtual networks communicate with external networks. The VLAN resource pool is planned during the configuration of the fabric global resource pool. | When creating a user gateway in a virtual network, select a resource from the fabric global resource pool to configure a user VLAN.
BD and VNI resource pools, which are used to divide Layer 2 broadcast domains in a virtual network and configure VBDIF interfaces as the gateway interfaces of user subnets. The BD and VNI resource pools are planned during the configuration of the fabric global resource pool. | When a user gateway is created in a virtual network, resources in the BD and VNI resource pools are automatically invoked to create a BD and the corresponding VBDIF interface.
User access point resource pool, which is planned during fabric access management configuration. This resource pool includes the authentication modes that can be configured on access points. | When configuring user access in a virtual network, you can select planned access point resources.
Egress pool, which contains the external resources that can be used by virtual networks. Two types of external resources are created during fabric configuration: External networks: used for virtual networks to communicate externally Network service resources: used for virtual networks to communicate with the authentication server and DHCP server, etc. | When creating a virtual network, you can select external networks and network service resources.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 48: Creating a Virtual Network
Creating a virtual network is to create a VPN instance to isolate different services.
Task | Procedure
Create a virtual network. | (Optional) Select network service resources for communication between the virtual network and network service resources (this step is typically performed). (Optional) Select an external network for communication between the virtual network and external network (this step is typically performed). Configure a user gateway, which can be manually specified or automatically allocated. Configure wired access: Select the access ports configured during fabric access management configuration, and add the ports to the service VLAN configured on the user gateway. Configure wireless access: Select the AC that connects to the wireless user subnet. Then the service VLAN configured on the user gateway will be delivered to the AC.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 49: Lab: Creating a Virtual Network (1)
Create a virtual network, define the virtual network name and user gateway location, and configure the external network and network service resources that the virtual network can access.
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
OA VN
RD VN
External network
Network service
resources
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 50: Lab: Creating a Virtual Network (2)
Define user gateways for the virtual network. User gateways can be manually created one by one by the network administrator or created in a batch through automatic allocation.
VN | Access User
OA | Sales_Wired: 172.17.10.0/24 Sales_Wireless: 172.17.11.0/24 Market_Wired: 172.17.20.0/24 Market_Wireless: 172.17.21.0/24
RD | RD: 172.17.30.0/24
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
OA VN
RD VN
External network
Network service
resources
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 51: Lab: Creating a Virtual Network (3)
Configure wired access.
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
OA VN
RD VN
External network
Network service
resources
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: User access is configured on the access points of the current virtual network.
Wired access: Users on the OA virtual network need to access the network through ACC_1 and ACC_2 and they all need to be authenticated. Therefore, in the wired access configuration, you need to select the interfaces on which authentication has been enabled on the two switches.

## Slide 52: Lab: Creating a Virtual Network (4)
Configure wireless access.
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
OA VN
RD VN
External network
Network service
resources
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: Wireless access: Select the border device in the wireless access configuration. The border device is a switch that provides the native AC, through which it manages APs and provides the wireless access service.

## Slide 53: Communication Between Virtual Networks
By default, virtual networks are isolated from each other. However, in some scenarios, they may need to communicate with each other, so reachable routes must be configured between them.
Configuring communication between virtual networks is to create static routes for VPN instances so that access users in different virtual networks can communicate with each other.
Task | Procedure
Configure communication between virtual networks. | Select interconnection devices. Select the interworking mode, including full interworking and partial interworking. Configure the source virtual network, source IPv4 prefix, destination virtual network, and destination IPv4 prefix.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 54: Lab: Configuring Virtual Network Interworking
Access the VN Interwork page, and click Add to configure interworking between virtual networks.
OA_VN
RD_VN
Fabric
Reachable routes
RD
172.17.30.0/24
Market_Wired
172.17.20.0/24
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 55: Service Deployment
On large campus networks, users are usually allowed access from any location, any VLAN, and any IP network segment with controlled network access rights.
Task | Procedure
Service deployment | Configure free mobility, including creating security groups, resource groups, and a policy control matrix. Configure access authentication, including creating user authentication accounts, authentication rules, authorization results, and authorization rules, as well as page management.
RD_VN
Fabric
RD
(802.1X)
OA_VN
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Sales_Wired
RD
Security group-based policy control matrix
Sales_
Wireless
Market_
Wired
Market_
Wireless
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
E_mail
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 56: Lab: Creating a Security Group
A security group is an entity unit for permission control. Users are assigned to different security groups, and access permissions are configured between security groups to implement user permission management on the network.
RD_VN
Fabric
RD
(802.1X)
OA_VN
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Sales_Wired
RD
Sales_
Wireless
Market_
Wired
Market_
Wireless
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 57: Lab: Creating a Resource Group
Different network service resources can be allocated to different resource groups. You can configure access permissions from security groups (source) to resource groups (destination) to manage the access to network service resources.
RD_VN
Fabric
RD
(802.1X)
OA_VN
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Sales_Wired
RD
Sales_
Wireless
Market_
Wired
Market_
Wireless
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
E_mail
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 58: Lab: Creating a Policy Control Matrix (1)
Administrators can define network-wide permission control policies based on security groups. An inter-group policy controls access between groups.
Select policy enforcement points for free mobility.
HQ
Border
Edge_1
ACC_1
Edge_2
AP1
PC1
PC2
PC3
ACC_2
Fabric
Policy enforcement point
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 59: Lab: Creating a Policy Control Matrix (2)
Administrators can define network-wide permission control policies based on security groups. An inter-group policy controls access between groups.
RD_VN
Fabric
RD
(802.1X)
OA_VN
Sales_
Wired
(802.1X)
Sales_
Wireless
(Portal)
Sales_Wired
RD
Security group-based policy control matrix
Sales_
Wireless
Market_
Wired
Market_
Wireless
Market_
Wired
(802.1X)
Market_
Wireless
(Portal)
E_mail
Policy control matrix: enables visualized management of communication policies between security groups on a campus network.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: When multiple policies are configured to control access from a source security group to multiple destination groups, the sequence in which these policies are matched can be determined based on the policy priority. For example, if the destination groups are resource groups, in which case the destination IP addresses may be the same, you need to manually adjust the policy priorities to ensure that a specific policy is matched first.

## Slide 60: Access Authentication
Task | Procedure
Configure 802.1X authentication. | Create user authentication accounts. Configure authentication rules. Configure authorization results and authorization rules.
Task | Procedure
Configure Portal authentication. | Create user authentication accounts. Configure authentication rules. Configure authorization results and authorization rules.
(Optional) Configure a MAC authentication exemption policy. | To enable a user client to be exempt from authentication based on its MAC address within a period after the client passes Portal authentication for the first time, configure a MAC authentication exemption policy in the user control policy.
802.1X authentication
802.1X is a port-based network access control protocol. It verifies user identities and controls access permissions of users on ports of LAN access devices.
When iMaster NCE-Campus functions as a RADIUS server, 802.1X authentication configuration on the server is illustrated in the following table:
Portal authentication
Portal authentication is also known as web authentication, and websites for Portal authentication are referred to as web portals. When a user accesses the network, the user must be authenticated on the web portal. If the user fails the authentication, the user can access only specified network resources. The user can access other network resources only after being authenticated successfully.
When iMaster NCE-Campus functions as the Portal server and RADIUS server, Portal authentication configuration on the server is illustrated in the following table:
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 61: Lab: Creating a User Group and Account
In the enterprise employee access scenario, user name and password authentication can be used to implement end user access.
During 802.1X and Portal authentication, users need to enter account information for authentication.
  Account: includes the user name and password. It is created by the administrator on iMaster NCE-Campus in advance.
1. Create a user group to which the user belongs.
2. Create an account in the matching user group.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: For example, when creating an account named kris (RD user), deselect Change password upon next login. As this user belongs to the RD user group, which does not require Portal authentication, deselect Portal in the Available login mode area.

## Slide 62: Lab: Configuring Authentication Rules
You can configure authentication rules to authenticate clients and users who access the network, ensuring network security.
iMaster NCE-Campus has a default authentication rule named Default. According to the rule, the local data source is used for authentication.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 63: Lab: Configuring Authorization Results
When configuring access authentication, you need to configure the rights obtained by users after they pass authentication.
In the authorization result, you can define the rights to be authorized to users, such as ACLs, security groups, URL filtering policies, and VLANs.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: After configuring authorization results, you need to bind the results to created sites.
iMaster NCE-Campus provides two default authorization results: permit access and deny access. Once selected, the default authorization result takes effect for all sites and cannot be modified or deleted.

## Slide 64: Lab: Configuring an Authorization Rule (1)
When authorizing a user who passes the authentication, the system matches the user against an authorization rule and grants specific permissions (called authorization results) to the user based on the matching rule.
1. Configure the authorization rule name, authentication mode, and access mode.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: An authorization rule defines authorization conditions. A user that matches the conditions can obtain the corresponding authorization result. That is, an authorization result specifies the permissions that a user can be granted after the user is authenticated successfully.
iMaster NCE-Campus provides a default authorization rule named default, in which the authorization result is deny access. The default authorization result can be modified to allow the use of another authorization result.

## Slide 65: Lab: Configuring an Authorization Rule (2)
2. Match users by user group information.
3. Bind the authorization result to the authorization rule.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 66: WLAN Service
In the distributed gateway solution, if the fabric uses a networking model where VXLAN is deployed across the core and aggregation layers and the border device provides the native AC function, APs need to go onboarded and get managed by the border device. APs on the campus need to broadcast an SSID for wireless access, and STAs that have associated with this SSID need to undergo Portal authentication.
HQ
Border
Native AC
Edge_1
ACC_1
AP1
PC1
PC2
PC3
VXLAN
ACC_2
Management IP address: 172.16.20.254
Management VLAN: VLAN 2
Edge_2
Task | Procedure
AP onboarding | Add APs to the HQ site and associate the APs with the border device. Create a management network segment and a management VLAN for AP onboarding. Configure the PnP management VLAN for wireless devices. Configure the source interface for the CAPWAP tunnel on the border device.
Wireless service configuration on the controller | Create wireless authentication and configure Portal authentication information.
Wireless service delivery (Web UI of the border device) | Configure an SSID profile. Configure a VAP profile, and bind the SSID profile and authentication profile to it. Bind the VAP profile to an AP group.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 67: Lab: AP Onboarding (1)
Choose Design > Device Management, and manually add a device to the HQ site. Set the protocol type to NETCONF, and add an AP by entering its ESN. As the AP is not onboarded, it is in the unregistered state.
Choose Provision > Site Configuration, select the Fit AP Management function of the switch, click the border device, and click Add to associate AP1 with the border device.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 68: Lab: AP Onboarding (2)
Choose Provision > Site Configuration, select the Subnet function of the switch, and create a subnet for AP onboarding. Through this subnet, the AP can obtain the IP addresses of the AC and controller.
1. Set the subnet name and management VLAN ID, select the method of obtaining the IP address of the AP, and set the management network segment of the AP.
2. Enable the DHCP function, set the AP working mode to Fit AP, and enable the controller address auto-negotiation and AC address auto-negotiation functions.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 69: Lab: AP Onboarding (3)
Choose Provision > Site Configuration, select the Management VLAN function of the site, and set the wireless PnP VLAN ID of the border device.
Then set the source address of the CAPWAP tunnel on the web UI of the border node. The AP can then obtain its own IP address, AC address, and controller address from the address pool of the VLANIF2 interface and successfully register with the border device and controller. After the registration, the AP status changes to normal.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 70: Lab: Wireless Service Configuration on the Controller (1)
Choose Provision > Site Configuration, select the Wireless Authentication function of the switch, and configure wireless authentication.
1. Set the wireless authentication name and SSID name, and select the authentication mode.
2. Set the page push mode, and select the Portal and RADIUS servers.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service
Notes: This example shows the wireless service configuration of sales personnel.

## Slide 71: Lab: Wireless Service Configuration on the Controller (2)
3. Select an authentication policy.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 72: Lab: Wireless Service Configuration on the Controller (3)
4. Select a security authentication policy.
5. Select a wireless authentication device.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 73: Lab: Wireless Service Delivery
Choose Design > Device Management, select the HQ site, and click the border device to access the border device management page.
Click Device Configuration to access the web UI of the border device.
The WLAN service configuration on the web UI of the border device is not provided here.
Site Management
Logical Network
Service Deployment
Fabric Network
Network Planning
Device Management
WLAN Service

## Slide 74
(Short-answer question) What site creation methods are supported by iMaster NCE-Campus?
(Multiple-answer question) Which of the following parameters can be entered in the fabric global resource pool? ( )
  VLAN
  Loopback interface IP address
  Bridge domain (BD)
  VXLAN network identifier (VNI)
Notes: Create sites one by one or in a batch.
  Create sites one by one: This mode applies when a small number of sites need to be added.
  Create sites in a batch: This mode applies when a large number of sites need to be added.
ACD

## Slide 75
This course introduces the process of deploying a virtualized campus network, and provides hands-on labs to help trainees understand the functions of the CloudCampus Solution and develop skills required for deploying a virtualized campus network.
Upon completion of this course, you will be able to deploy the virtualized campus network solution on your own and perform network O&M and management.