## Slide 1
Datacom
General
V1.0
Wuyue/WWX291773
2021.4
Li Xianzhi/l00354681
New
Wuyue/WWX291773
2021.9
He Junjian/WX580230
Update

## Slide 2: WAN Interconnection Solution and Technology Overview

## Slide 3
Wide area networks (WANs) have undergone a long history, and the technologies used on WANs have been updated many times. Enterprises have more diversified requirements over WANs than campus networks. In addition, the requirements for network connection mode, reliability, and security vary with enterprises.
To meet the interconnection requirements of different enterprises, a variety of WAN interconnection technologies are developed.
This course will focus on the WAN interconnection technologies and their application scenarios.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the basic architecture of a typical WAN interconnection solution.
  Describe WAN interconnection networking technologies and their application scenarios.
  Describe WAN interconnection reliability technologies and their application scenarios.
  Describe WAN interconnection optimization technologies and their application scenarios.

## Slide 5
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 6: What Is a WAN?
WANs provide interconnection services across regions, cities, and countries. A WAN usually spans a long distance (dozens or even thousands of kilometers). To meet long-distance transmission requirements on a WAN, optical fibers are often used as the interconnection media.
DC
Branch
HQ
Residents
LAN
WAN
LAN
ISP
Notes: LAN
  A local area network (LAN) is a computer network that connects computers, peripheral devices, databases, and other devices in a limited geographical area (such as a campus, factory, or organization) within thousands of meters.
WAN
  WANs provide wider coverage than LANs and metropolitan area networks (MANs). The communication subnet of a WAN mainly uses the packet switching technology. The communication subnet of a WAN can use the public packet switching network, satellite communication network, and wireless packet switching network to interconnect the LANs or computer systems in different areas for resource sharing.
  The Internet is the largest WAN in the world.
Relationship between the LAN and WAN:
  A LAN is located in an area, whereas a WAN spans a larger area. For example, the headquarters of a large company is located in Beijing, and its branches are distributed all over the country. If the company connects all its branches through a network, a branch is a LAN, and the company network is a WAN.

## Slide 7
Notes:   Typical WAN rates range from 56 kbit/s to 155 Mbit/s. Currently, 622 Mbit/s, 2.4 Gbit/s, and even higher rates are available. The transmission delay ranges from several milliseconds to hundreds of milliseconds (when satellite channels are used).

## Slide 8: WAN and Enterprise WAN Interconnection
Enterprise WAN interconnection refers to the interconnection between nodes at different levels, such as the headquarters (HQ), data centers (DCs), branches, fixed offices, and mobile offices within enterprises.
Generally, enterprise WAN interconnection depends on a carrier-built or self-built WAN.
Carrier network/Self-built network
Branch site
Branch site
HQ
Branch site
Enterprise WAN interconnection
WAN

## Slide 9: Major Enterprise WAN Interconnection Modes
Generally, enterprise WANs can be interconnected in the following modes:
  Carriers' transmission or MPLS private lines are used to connect regional networks. This mode is expensive and is applicable to enterprises with high SLA requirements.
  The carrier Internet + VPN technology is used for connection. This mode is applicable to small- and medium-sized branches that do not have high SLA requirements.
  Carriers' point-to-point (P2P) private lines are used to implement cross-city or cross-border connections. This mode is mainly used for connections between DCs, headquarters, or important branches, and is expensive.
  Industries such as electric power and transportation build network connections through self-built private lines.
Usually, enterprise WANs are interconnected using a combination of the preceding modes.
Enterprise WAN interconnection networking
HQ
Branch site
Transmission private line
MPLS private line
4G/5G
Internet
Self-built private line
Branch site
Branch site
HQ
Notes: SLA is an agreement between the network service provider and the customer. It defines terms such as service type, service quality, and customer payment.
According to the SLA requirements, the service provider uses multiple technologies and solutions to monitor and manage the network performance and traffic so as to meet the requirements defined in the SLA and generate reports about customers' network performance.

## Slide 10: Enterprise WAN Interconnection Technologies: Carriers' Private Lines
To ensure network reliability and security, enterprises lease transmission or MPLS private lines from carriers when constructing enterprise WANs.
  Transmission private lines are expensive, but data is carried on dedicated lines, ensuring service quality and security.
  MPLS private lines are cheaper than transmission private lines and can ensure service security. However, service reliability is not as good as that of transmission private lines.
  A small number of enterprises (such as transportation and electric power enterprises) can deploy optical fibers and build their own backbone networks.
Leasing private lines from carriers
Enterprise HQ
Branch site
Branch site
Branch site
Enterprise HQ
Branch site
Bare fiber/SDH/MSTP/WDM
MPLS private line
MPLS L2VPN/L3VPN
Transmission private line

## Slide 11: Enterprise WAN Interconnection Technologies: Internet and VPN
With the development of the Internet, some enterprise services can be carried over the Internet.
The Internet has security risks, so VPN technology is used to provide secure and reliable connections.
Virtual Private Dial-up Network (VPDN) technologies, such as Point-to-Point Tunneling Protocol (PPTP), Layer 2 Tunneling Protocol (L2TP), and Point-to-Point Protocol over Ethernet (PPPoE), allow terminal users or branches to dial up to the carrier network or HQ network.
Typically, Internet Protocol security virtual private network (IPsec VPN) technology is used to build network connections between enterprise branches or between enterprise branches and the HQ.
To simplify IPsec configuration on large-scale networks, technologies such as Dynamic Smart VPN (DSVPN) and Any to Any (A2A) VPN have been developed and widely used.
Internet and VPN technologies
Enterprise HQ
Branch site
Internet
Branch site
Branch site
Enterprise HQ
PPTP/L2TP/SSL VPN/IPsec VPN/DSVPN/A2A VPN

## Slide 12: Common Application Scenarios of Enterprise WAN Interconnection Networking
Enterprise WAN interconnection needs to be deployed based on enterprise requirements. For example, in the financial service industry, most enterprises lease transmission or MPLS private lines to guarantee network reliability and security. Considering network costs, other enterprises usually lease MPLS private lines as primary lines and Internet + VPN lines as backup lines.
WAN interconnection in the financial service industry
Core backbone network
Level-1 branch
Level-2 branch
Sub-branch
Sub-branch
Level-2 branch
ATM
Sub-branch
Branch service network
Branch LAN
Branch LAN
SDH/MSTP/MPLS
SDH/MSTP/MPLS
SDH/MSTP/MPLS
WAN interconnection for a wine enterprise
Branch in area A
Internet (backup)
MPLS (primary)
Branch in area B
Branch in area C
GRE over IPsec
Enterprise HQ
Enterprise HQ

## Slide 13
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
  WAN Interconnection Networking Solution
  Private Line Technologies and Their Applications
  VPN Technologies and Their Applications
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 14: Enterprise WAN Interconnection Networking Solution
There are many interconnection modes for enterprise WANs. Generally, one or more interconnection modes are used based on different enterprise requirements.
Enterprise branch
MPLS private line
HQ
Enterprise branch
Enterprise branch
Bare fiber/SDH/WDM/MSTP
L2TP/SSL VPN
MPLS VPN
PE
PE
P
DSVPN/IPsec VPN
CE
CE
CE
4G/5G
Transmission private line
Internet
Enterprise branch

## Slide 15: Comparison Between Private Line and VPN Technologies
Private lines were introduced very early. They can meet interconnection requirements of enterprises and ensure high network reliability and security. However, private lines are expensive.
As networks develop, VPN technologies start to occupy more market shares. However, some industries demanding high security and reliability, such as the financial service industry, still prefer private line technologies.
Selecting private line or VPN technologies depend on enterprises' services. The following table compares the two technologies.
Item | Private Line Technology | VPN Technology
Security | Relatively high: depending on ISPs | Very high: Data is encrypted before being transmitted and security control is in the hands of users.
Reliability | High: depending on ISP network reliability | Comparatively high: depending on reliability of Internet lines
Scalability | Medium: depending on ISPs | Based on TCP/IP technology, the access mode is flexible. A network can be scaled out as long as it is reachable.
Investment cost | The private line expense is very high and needs to be paid every month. In addition, the device expense needs to be invested in the initial period of network construction. | One-off device expense is invested, so there is no need to pay monthly operating expenses.
Support for mobile users | Mobile users can only connect to the network to which private lines are reachable, and internal mobile users leaving a LAN cannot access a private network. | Internal mobile users can use the Internet for secure access, eliminating geographical differences.
Transmission bandwidth | Leased bandwidth is low because of the high price. | The Internet is cheap, and the leased bandwidth is high.

## Slide 16: Overview of Carriers' Private Lines
Carriers have a large number of line resources and launch different private line services based on different industries and scenarios.
Carriers' high-quality transmission private line services mainly include SDH, MSTP, and bare fiber services, which are expensive but deliver excellent performance.
MPLS VPN is another type of private line services provided by carriers. MPLS VPN private lines provide slightly lower performance than transmission private lines but are less expensive.
Carrier's private line (private line network in the financial service industry)
Level-1 branch
Level-2 branch
Sub-branch
Sub-branch
Level-2 branch
ATM
Sub-branch
Branch service network
Branch LAN
Branch LAN
The financial service industry leases carriers' MSTP/SDH private line services to ensure high network reliability.
MSTP/SDH
MSTP/SDH
Carrier's private line (MPLS VPN network of a provincial library)
County library
County library
County library
Community library
Community library
Community library
Community library
City library
City library
GRE over IPsec (enterprise-built)
MPLS VPN (ISP)
MPLS VPN (ISP)

## Slide 17: Overview of Enterprise-Built Private Line and VPN
Enterprises can establish VPNs, such as SSL VPN, DSVPN, and IPsec VPN, through carriers' networks.
Some large enterprises can lay out optical fibers by themselves and set up private lines. However, only few enterprises can lay out optical fibers by themselves.
VPNs built by enterprises are more and more widely used because they are cost-effective, easy to expand, and controllable.
Enterprise-built VPN (VPN of a provincial library)
Enterprise-built private line (MPLS VPN network of the energy industry)
County library
County library
County library
Community library
Community library
Community library
Community library
Municipal library
Municipal library
GRE over IPsec
MPLS VPN (ISP)
MPLS VPN (ISP)
Provincial backbone network
Provincial backbone network
National backbone network
Municipal service network
Municipal service network
Municipal service network
Municipal service network
MPLS VPN (self-built)
MPLS VPN (self-built)

## Slide 18
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
  WAN Interconnection Networking Solution
  Private Line Technologies and Their Applications
  VPN Technologies and Their Applications
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 19: Overview of Private Line Technologies
Private line technologies were introduced very early. As networks develop, many private line technologies, such as frame relay (FR) and ATM, are no longer used. Currently, the following private line technologies are widely used:
  Bare fiber: Carriers provide bare fibers along which no intermediate device is deployed. Therefore, bare fibers are expensive.
  SDH/MSTP/WDM: Transmission private lines use transmission devices to build hard pipes over optical fibers, ensuring good performance. The price of such private lines is lower than that of bare fibers.
  MPLS VPN: MPLS private lines use Ethernet for network access and do not have hard pipes. The performance of MPLS VPN is poorer than that of transmission private lines, but MPLS VPN is the cheapest among all types of private lines.

## Slide 20: Overview of Bare Fibers
A carrier provides a bare fiber line along with no intermediate device is deployed. The network capacity depends on the enterprise devices at both ends of the bare fiber.
Bare fibers are charged based on the distance. A longer distance indicates a higher cost. Generally, the maximum transmission distance of a hop of an optical fiber is 300 km. If the distance between two sites exceeds 300 km, a regeneration device needs to be deployed.
Enterprise branch
Enterprise HQ
Carrier
Optical network
Transmission device
Transmission device

## Slide 21: Exemplary Application Scenario of Bare Fibers
Application scenario of bare fibers
Carriers' bare fibers can be leased to build network connections between the main campus and branch campus in the same city. This practice simplifies network management and access authentication management.
ISP1
ISP2
Lease carriers' bare fibers
Main campus
Branch campus

## Slide 22: Overview of SDH/MSTP/WDM Private Lines
Enterprises that require long-distance transmission and high network reliability and security can lease SDH/MSTP/WDM private lines.
This type of private line is a transmission private line. Tenants exclusively occupy part of the bandwidth of the transmission private line. Because multiple users share the transmission private line, its price is lower than that of bare fibers. Although transmission private lines are shared by tenants, they exclusively occupy bandwidth and use hard pipes. Therefore, they deliver high network reliability and security.
MSTP and WDM private lines are widely used on the live network, and SDH private lines are still used in a few areas.
Enterprise branch
Enterprise HQ
Carrier
Transport network
SDH/MSTP/WDM device
SDH/MSTP/WDM device
Notes: SDH is a TDM system and a traditional circuit scheduling mode.
The multi-service transport platform (MSTP) receives, processes, and transmits TDM, ATM, and Ethernet services.
WDM uses multiple lasers to transmit multiple beams of lasers with different wavelengths over a single optical fiber. The transmission bandwidth of WDM devices is high, and the live-network bandwidth can reach up to 8 Tbit/s.

## Slide 23: Exemplary Application Scenario of SDH/MSTP/WDM Private Lines
Application scenario of SDH/MSTP/WDM private lines
To ensure high reliability and security, MSTP or SDH private lines are used for interconnection between financial service branches.
MSTP/SDH
MSTP/SDH
MSTP/SDH
HQ
Branch
Branch
Sub-branch
Sub-branch

## Slide 24: MPLS VPN Private Line
Backbone
MPLS VPN technology is widely used in enterprise interconnection scenarios. MPLS L2VPN or MPLS L3VPN can be deployed based on enterprise requirements. MPLS VPN makes a compromise between the cost and performance, so it is very popular.
For enterprises that can build their own WANs, such as railways and electric power companies, MPLS VPN is an easy-to-manage and low-cost VPN technology. For enterprises that cannot build their own WANs, MPLS VPN is expensive.
The enterprises that require high network reliability and security can use the MPLS VPN private line as the primary link and the GRE over IPsec line as the backup link.
Branch
MPLS VPN
PE
PE
P
CE
HQ
CE

## Slide 25: Exemplary Application Scenario of MPLS VPN
Application scenario of MPLS VPN
The MPLS L3VPN solution is widely used on the live network. Some large networks may use inter-AS MPLS L3VPN.
Provincial backbone network
Provincial backbone network
PE
PE
PE
PE
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
ASBR
Enterprise A
Enterprise B
Enterprise A
Enterprise B
RR
RR
RR
RR
RR
RR
Core backbone network
VPNv4 peer
MPLS L3VPN traffic
Notes: There are three types of inter-AS MPLS L3VPN solutions: Option A, Option B, and Option C.
Option A applies to small inter-AS MPLS L3VPNs. Option B applies to midsize and large inter-AS MPLS L3VPNs. Option C applies to large or super-large inter-AS MPLS L3VPNs.

## Slide 26
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
  WAN Interconnection Networking Solution
  Private Line Technologies and Their Applications
  VPN Technologies and Their Applications
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 27: Overview of VPN Technologies
VPN technologies are widely used in scenarios where enterprises build their own Internet.
VPN technologies can be classified into the following three types based on the service usage:
  Access VPN (virtual private network for remote access): also called dial-up VPN or VPDN. Generally, L2TP VPN technology is used.
  Intranet VPN (internal virtual private network of an enterprise): connects gateways and connects resources of the same company through the company's network architecture. Generally, GRE or DSVPN technology is used.
  Extranet VPN (extended internal virtual private network of an enterprise): is used to build an extranet with the enterprise network of a partner. Generally, SSL VPN technology is used.
Notes: By service usage:
  Access VPN: enables mobile employees, remote office employees, and remote small offices to establish private network connections with enterprise intranet and extranet through a public network. There are two types of access VPN connections: client-initiated and NAS-initiated.
  Intranet VPN: Intranet VPN is an extension or replacement of traditional private lines or other enterprise networks to connect distribution points within an enterprise through a public network.
  Extranet VPN: extends enterprise networks to suppliers, partners, and even clients over a public network.
According to the layers of tunnels in the OSI model:
  Layer 2 tunneling protocol: encapsulates PPP frames into a tunnel. Layer 2 tunneling protocols include the Point-to-Point Tunneling Protocol (PPTP), Layer 2 Forwarding (L2F), and Layer 2 Tunneling Protocol (L2TP).
  Layer 3 tunneling protocol: Only Layer 3 packets are carried in a tunnel. Existing Layer 3 tunneling protocols include Generic Routing Encapsulation (GRE) and IPsec. IPsec includes the Authentication Header (AH) protocol and Encapsulating Security Payload (ESP) protocol.

## Slide 28: Access VPN Overview
Access VPN uses virtual private dial-up network (VPDN) technology, and is a type of VPN service based on dial-ups. It can be used for enterprise interconnection or remote access to enterprise networks.
VPDN tunnel
VPDN tunnel
VPDN
PC
PC
PC
PC
Enterprise branch
Enterprise HQ
Dialing user
Dial-up network
NAS
(LAC)
LNS
RADIUS server
RADIUS server
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: VPDN is implemented by using a tunneling technology. That is, data of an enterprise network is encapsulated in a tunnel for transmission. On an interface between the source LAN and public network, the tunneling technology encapsulates data as a payload in a data format that can be transmitted on a public network. On an interface between the destination LAN and the public network, it decapsulates data to extract the payload. The logical path through which encapsulated data packets are transmitted on the Internet is called a tunnel. To ensure that data is encapsulated, transmitted, and decapsulated smoothly, the communication protocol is the core.
VPDN provides three common tunneling technologies:
  Point-to-Point Tunneling Protocol (PPTP)
  Layer 2 Forwarding (L2F)
  Layer 2 Tunneling Protocol (L2TP)

## Slide 29: PPTP Overview
PPTP is a type of VPN protocol and has a history of more than 20 years. This protocol relies on encryption, authentication, and Point-to-Point Protocol (PPP) for negotiation. It requires only the user name, password, and server address for connection setup.
PPTP is fast, but has weak encryption. Among all VPN protocols, PPTP has the lowest encryption level and must be based on IP networks.
Internet
PC
PC
PPTP
client
PPTP
client
PPTP tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 30: L2TP Overview
L2TP, an open standard of IETF, combines advantages of PPTP. L2TP is especially suitable for setting up an access VPN and has become a de facto industry standard.
L2TP is only a tunneling protocol and does not provide encryption or privacy protection. Therefore, L2TP is usually used together with IPsec.
L2TP is one of commonly used enterprise interconnection technologies. When L2TP is used, an AAA server is required. L2TP is a good choice for constructing an L2VPN.
Internet
LNS
L2TP client
(LAC)
Enterprise branch
Enterprise HQ
L2TP tunnel
L2TP tunnel
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 31: Live-Network Application of Access VPN
Access VPN is mainly used for remote access of intranet users, and L2TP over IPsec is most widely used.
PPTP requires the support of the Windows operating system. In addition, the IP address of the Windows server on the intranet needs to be mapped through NAT for extranet access. Therefore, PPTP is difficult to deploy and is seldom used.
Live-network application of L2TP over IPsec
L2TP connections can also be used between branch sites. However, L2TP cannot transmit multicast data or advertise routes between the HQ and branches. Therefore, L2TP is mainly used for remote user access on the live network.
Enterprise HQ
Internet
LNS
Traveling employee
Traveling employee
L2TP over IPsec
L2TP over IPsec
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 32: Intranet VPN Overview
Internet
Intranet VPN technology is used to construct a VPN between gateways based on the Internet. GRE and DSVPN technologies are mainly used.
GRE and DSVPN technologies are used to establish VPNs between enterprise branches and the HQ.
PC
PC
PC
PC
Enterprise branch
Enterprise HQ
PC
PC
Enterprise branch
GRE, DSVPN
GRE, DSVPN
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: Intranet VPN mainly uses the following technologies:
  GRE
  GRE over IPsec
  DSVPN
  DSVPN IPsec

## Slide 33: GRE Overview
Generic Routing Encapsulation (GRE) is used to encapsulate packets of some network-layer protocols (such as IP, IPX, and AppleTalk) so that the encapsulated packets can be transmitted over the network on which another network-layer protocol is applied.
GRE is typically used on networks with a few branch sites.
Internet
Link layer
GRE
IP
IP
Payload
Flags
Protocol Type
Internet
PC
PC
PC
PC
Enterprise branch
Enterprise HQ
GRE Tunnel
RTA
RTB
GRE packet
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: GRE is a Layer 3 tunneling technology. A GRE tunnel is a virtual P2P connection that transmits encapsulated data packets.
The two ends of a GRE tunnel are tunnel interfaces which encapsulate and decapsulate data packets. The tunnel interface that sends encapsulated packets is called the tunnel source interface, and the one that receives these packets on the peer end is called the tunnel destination interface.
The packet encapsulation process in the figure is as follows:
  After receiving an IP packet, RTA's interface that connects to the enterprise branch sends a packet to the IP protocol module.
  The IP protocol module checks the destination address in the packet header to determine how to forward this packet. If the packet is destined for the other end of the GRE tunnel, the IP protocol module sends the packet to the tunnel interface.
  After receiving the packet, the tunnel interface encapsulates the packet using GRE and delivers the packet to the IP protocol module.

## Slide 34
Notes:   The IP protocol module encapsulates the GRE packet using a new IP packet header. The source address is the address of the tunnel source interface, and the destination address is the address of the tunnel destination interface. Then the IP protocol module forwards the encapsulated IP packet from the WAN interface (tunnel source interface) based on the destination address and routing table.
As the reverse of encapsulation, the decapsulation process is as follows:
  RTB receives an IP packet from its physical interface connected to the Internet and checks the destination address. If the destination is RTB and the protocol ID in the IP packet header is 47 (indicating GRE packet), RTB removes the IP packet header and sends the packet to the GRE module.
  The GRE module verifies the checksum and key fields, removes the GRE header, and sends the packet to the IP protocol module.
  The IP protocol module forwards the packet to the enterprise HQ.

## Slide 35: GRE over IPsec Overview
GRE does not support encryption. IPsec supports only the IP protocol and does not support multicast.
GRE over IPsec combines advantages of both GRE and IPsec, and offsets their disadvantages.
GRE over IPsec is a point-to-point VPN technology commonly used by enterprises.
Internet
PC
PC
PC
PC
IPsec tunnel
IPsec tunnel (external)
GRE tunnel
GRE tunnel (internal)
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: GRE encapsulates multicast data to allow data to be transmitted through GRE tunnels. Currently, IPsec can encrypt only unicast data. If multicast data, such as routing protocol, voice, and video data, needs to be transmitted over IPsec tunnels, a GRE tunnel can be established to encapsulate multicast data, and then IPsec encrypts the encapsulated packets. In this way, multicast data is encrypted and transmitted in the IPsec tunnel.
GRE over IPsec combines advantages of both GRE and IPsec. It enables a network to support multiple upper-layer protocols and multicast packets, as well as packet encryption, identity authentication, and data integrity check.
GRE over IPsec encapsulates packets using GRE, and then IPsec.
GRE over IPsec supports the following encapsulation modes:
  Tunnel mode
  Transport mode

## Slide 36: DSVPN Overview
DSVPN overcomes defects of GRE over IPsec and enables enterprises with a large number of branches to easily build VPNs.
DSVPN is a technology that dynamically establishes GRE tunnels. It uses the Next Hop Resolution Protocol (NHRP) to dynamically collect, maintain, and advertise information such as the public IP address of each spoke, allowing the source branch to obtain the public IP address of the destination branch.
DSVPN uses mGRE technology to enable VPN tunnels to transmit multicast and broadcast packets, and a tunnel interface can establish VPN tunnels with multiple peers.
The GRE tunnel established by DSVPN can still use IPsec technology to ensure tunnel security.
Hub
Spoke
Spoke
Spoke
Dynamic mGRE tunnel
Data between spokes
Static mGRE tunnel
Internet
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: DSVPN resolves the following defects of GRE over IPsec:
  All traffic must pass through the hub.
  The hub configuration needs to be modified when a site is added.
  If spokes use dynamic addresses, problems may occur when P2P GRE is deployed.

## Slide 37: Live-Network Application of Intranet VPN
On the live network, intranet VPN is mainly used for interconnection between enterprise branches and the HQ or between branches.
GRE over IPsec is widely used on the live network. For enterprises with many branches, Efficient VPN can be used to simplify the branch configuration. IPsec link redundancy can be deployed to ensure GRE reliability.
Live-network application of GRE over IPsec
DSVPN is seldom used on the live network due to the following reasons: 1. Many enterprises expect that traffic between branches can pass through the HQ to facilitate management. 2. Enterprise O&M personnel just have a basic understanding of DSVPN, which is inconvenient for O&M.
Enterprise HQ
Internet
Branch
Branch
GRE over IPsec
GRE over IPsec
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 38: Extranet VPN Overview
Internet
Extranet VPN is mainly used to deliver secure network access between customers or suppliers. Traveling employees can also use extranet VPN to access the enterprise network.
Extranet VPN mainly uses SSL VPN and L2TP.
PC
PC
PC
PC
Customer
Enterprise HQ
SSL VPN/L2TP
SSL VPN/L2TP
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 39: SSL VPN Overview
Internet
SSL VPN is mainly used to enable traveling employees to remotely access the enterprise intranet, which is an extension of the enterprise intranet on the WAN.
SSL VPN authenticates and controls users based on HTTP. Users do not need to configure SSL VPN, which is easy to use.
SSL VPN tunnel
SSL VPN client
SSL VPN gateway
Web page proxy
File sharing
Port forwarding
Network extension
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview
Notes: SSL VPN is a VPN remote access technology based on SSL. Mobile users (referred to as remote users in SSL VPN) can use SSL VPN to securely and conveniently access enterprise intranets and intranet resources, improving work efficiency.
Before SSL VPN is developed, VPN technologies such as IPsec and L2TP are used to enable remote user access. However, these VPN technologies have the following disadvantages:
  Remote users need to install specific client software on their terminals, leading to difficult network deployment and maintenance.
  The IPsec or L2TP VPN configuration is complex.
  Network management personnel cannot perform fine-tuned control over the remote users' access permission to enterprise intranet resources.

## Slide 40: Exemplary Application Scenario of Extranet VPN
It is convenient for external users to access the intranet through SSL VPN. They can directly access the intranet after passing web page authentication, without having to install a client. In addition, there are many SSL VPN service options, such as web page proxy, file sharing, port forwarding, and network extension.
Application scenario of SSL VPN
SSL VPN is easy to use. You can use a browser to access the enterprise intranet. However, not all routers support SSL VPN. For routers that do not support SSL VPN, you can use L2TP to establish connections between the extranet and intranet.
Remote office
Partner
Mobile user
Port 443
Internet
HQ
Web page server
OA
Email server
ERP
FTP server
NMS
Branch user
Partner
Network extension
Web page proxy
File sharing
Port forwarding
SSL VPN gateway
Access VPN Overview
Intranet VPN Overview
Extranet VPN Overview

## Slide 41
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
Reliability Technologies and Their Applications of WAN Interconnection
  Link Detection Technologies and Their Applications
  Network and Service Reliability Technologies and Their Applications
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 42: Overview of Link Detection
Fluctuation of network link quality affects service quality. How to quickly detect the link quality fluctuation is the first step in improving link quality.
There are many protocols and technologies for detecting link quality, which are classified into two types:
  Link connectivity detection technologies:
    Bidirectional Forwarding Detection (BFD)
    Ethernet in the First Mile (EFM)
    Connectivity Fault Management (CFM)
  Link quality detection technologies:
    Network Quality Analysis (NQA)
    IP Flow Performance Measurement (IP FPM)
BFD, EFM, and CFM are used to detect network link connectivity.
NQA and IP FPM are used to detect network quality.
BFD, EFM, CFM
NQA, IP FPM
On the live network, BFD is typically used to detect link connectivity, and NQA or IP FPM is typically used to detect link quality.

## Slide 43: Overview of BFD
BFD provides a universal, standardized, media-independent, and protocol-independent fast failure detection mechanism. It has the following advantages:
  Provides low-overhead and fast failure detection for channels between adjacent forwarding engines.
  Performs uniform detection for all media and protocol layers in real time.
BFD is a simple Hello protocol. Two systems establish a BFD session channel and periodically send BFD packets to each other. If one system does not receive BFD packets from the other system within a certain period, the system considers that a fault occurs on the channel.
Application layer
Transport layer
Network layer
Data link layer
Physical layer
Application layer
Transport layer
Network layer
Data link layer
Physical layer
BFD session detection
Notes: Only one BFD session can be established in a data path. If different applications need to use different BFD parameters on the same data path, use the BFD parameters that can meet the requirements of all applications to configure a unique BFD session and enable the status changes of the BFD session to be reported to all the applications bound with the BFD session.

## Slide 44: Overview of NQA
To visualize the quality of network services and allow users to check whether the quality of network services meets requirements, the following measures must be taken:
  Enable devices to provide network service quality information.
  Deploy probe devices to monitor network service quality.
The preceding measures require devices to provide statistical parameters such as the delay, jitter, and packet loss rate and require dedicated probe devices. These requirements increase investments on devices.
When NQA is deployed on devices, dedicated probe devices do not need to be deployed, effectively reducing costs. NQA can accurately test the network running status and output statistics.
NQA measures network performance and collects statistics about the response time, network jitter, and packet loss rate in real time.
TCP delay detection
DNS delay detection
Total HTTP delay detection
NQA test
NQA client
NQA server
Notes: Additionally, NQA measures the performance of different protocols running on the network. This facilitates real-time collection of network performance counters, such as the total HTTP connection delay, TCP connection delay, DNS resolution delay, file transfer rate, FTP connection delay, and DNS resolution error rate.

## Slide 45: Overview of IP FPM
With the advent of the cloud computing era, end-to-end service performance measurement becomes essential. However, the commonly used NQA technology has the following defects in end-to-end network performance measurement scenarios:
  NQA simulates service packet forwarding on the network by constructing service packets. Therefore, the collected performance statistics are not accurate.
  NQA does not support end-to-end performance measurement across network layers, and cannot monitor or measure network performance in a multipath scenario of IP networks.
IP flow performance measurement (IP FPM) can effectively solve these problems. It is a general IP network performance measurement solution. IP FPM can directly measure service packets, and the measurement data can reflect the performance of IP networks. In addition, IP FPM can monitor the changes of services carried by IP networks online and accurately reflect the running status of services.
DCP
DCP
MCP
TLP
TLP
Data
IP Header
Data
IP Header
IP FPM colors data packets.
NMS/Controller
The DCP sends the statistics collected by the TLP to the MCP.
The TLP calculates the number of colored packets.
The TLP calculates the number of colored packets.
The DCP sends the statistics collected by the TLP to the MCP.
The MCP summarizes the statistics and calculates the packet loss rate and delay.
(Optional) The MCP reports results to the NMS or controller.
1
2
2
3
3
4
5
Notes: TLP is short for Target Logical Port.
  TLPs are interfaces on the edge nodes of the network and provide the following functions:
    Collect statistics about the packet loss rate and delay.
    Generate statistics, such as the number of packets sent and received, volume of traffic sent and received, and timestamp.
  An In-Point-TLP collects statistics about service flows it receives. An Out-Point-TLP collects statistics about service flows it sends.
DCP is short for Data Collecting Point.
  DCPs are edge nodes on the network and provide the following functions:
    Manage and control TLPs.
    Collect the statistics generated by TLPs.
    Report the statistics to an MCP.

## Slide 46
Notes: MCP is short for Measurement Control Point.
  MCPs are intermediate nodes on the network and provide the following functions:
    Collect the statistics reported by DCPs.
    Summarize and calculate the statistics.
    Report the statistics to user terminals or the NMS.

## Slide 47: Exemplary Application Scenarios of Link Detection
Common link quality detection scenario
NQA and BFD are usually associated with floating routes.
When NQA or BFD detects a link fault, the high-priority route becomes invalid and the backup route is used.
E2E link quality detection
IP FPM colors and marks data packets to help ingress and egress devices measure the packet loss or jitter of specific traffic.
IP FPM can measure end-to-end network quality. Therefore, it can measure the actual network quality of different links in the multi-link egress scenario.
ISP1
ISP2
ISP1
ISP2
IP routing-table
Net1 60 ISP1 Track BFD/NQA
Net1 100 ISP2
The primary path is ISP1 and BFD or NQA is used to monitor the link.
The backup path is ISP2.
BFD
NQA
Incoming traffic
Outgoing traffic
IP FPM is used to test incoming and outgoing traffic.
IP FPM is used to test incoming and outgoing traffic.

## Slide 48
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
Reliability Technologies and Their Applications of WAN Interconnection
  Link Detection Technologies and Their Applications
  Network and Service Reliability Technologies and Their Applications
Optimization Technologies and Their Applications of WAN Interconnection

## Slide 49: Overview of Network Reliability
If a fault occurs on the network, the fault may not be detected or rectified in a timely manner. To resolve this issue, redundancy technologies are required.
Common redundancy technologies include stack, link aggregation, and VRRP.
VRRP is the most widely used network redundancy technology on egress devices or gateways.
VRRP
Stack
Link aggregation

## Slide 50: Overview of VRRP
Hosts are connected to external networks through gateways. If a single gateway fails, services will be interrupted for a long time. Adding egress gateways is a common method to improve system reliability. In this case, route selection among multiple egresses becomes essential.
VRRP groups multiple routing devices into a single virtual routing device. If a gateway fails, VRRP selects a new gateway to transmit data traffic, ensuring high network reliability.
Internet
VRRP
Only one device provides services externally.
Master
Backup
The master device forwards the traffic sent by hosts.
Internet
VRRP
Master
Backup -> Master
The downlink of the master device is disconnected, so the master device cannot provide gateway services.
The backup device becomes the new master device, and traffic is switched to it.
The backup device does not transmit traffic.
PC1
PC2
PC1
PC2
The master device fails.

## Slide 51: Service Reliability
In the cloud computing era, network reliability cannot meet user requirements. Users want to understand the live network status based on applications and adjust the network based on the application status.
Such requirements pose the following challenges to traditional networks:
  Traditional networks cannot accurately identify applications.
  Traditional networks cannot be adjusted based on applications.
To cope with the challenges, two technologies are developed:
  Smart Application Control (SAC): This technology can flexibly identify applications.
  Smart Policy Routing (SPR): This technology can switch forwarding paths based on the network or application status.

## Slide 52: Overview of SAC
Typically, routing and switching devices cannot identify application-layer information. Therefore, it is difficult to manage networks based on applications. SAC technology helps routing and switching devices identify classified applications.
SAC uses service awareness (SA) and first packet identification (FPI) technologies to detect and identify Layer 4 to Layer 7 information (such as HTTP and RTP) in packets.
Network device
FPI signature database
Service traffic
Signature matching
SA signature database
Signature matching
Application identification record
SAC identification
Traffic is directly forwarded at Layer 3 if the application has been identified.
Voice
Video
Web page
Download
Forwarding table
SAC application identification process
Notes: After a packet enters an SAC-enabled device, the device determines whether the corresponding application has been identified based on the 5-tuple information carried in the packet. If the application has been identified, the device forwards the packet at Layer 3 without identifying the application again. If the application has not been identified, the device performs SAC application identification. The device then processes the packet based on the SAC identification result and forwards the packet at Layer 3. The SAC application identification process is as follows: The device identifies an application based on the ACL rules defined in FPI. If the application cannot be identified, the device identifies the application based on the DNS entries defined in FPI. If the application still cannot be identified, the device identifies the application based on the protocol and port mapping table defined in FPI. If the application still cannot be identified, the device starts the SA identification process.

## Slide 53: Overview of SPR
In the cloud computing era, more users shift their attention from network connectivity to service availability, such as service response speed and service quality. However, traditional networks cannot detect link quality and service requirements, resulting in poor user experience.
SPR addresses this problem. It actively detects the link quality and matches service requirements to select an optimal link to forward service data. SPR prevents network blackholes and flappings.
NQA
IP FPM
HQ
Branch
NQA
IP FPM
SRP deployment
SRP deployment

## Slide 54: Exemplary Application Scenario of Service Reliability Technologies
Deploying both SAC and SPR can ensure the reliability of specific services on the network.
  SAC uses the SA signature database and FPI signature database to identify applications and group traffic.
  SPR determines the link quality and forwarding path based on the probe packets.
MPLS
Internet
Video application
Internet access
Audio application
SAC function module
Application identification
Application-based traffic steering
SPR function module
Link detection
Link detection
Application scenario of service reliability technologies

## Slide 55
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection
  QoS Technology and Its Application
  FEC Technology and Its Application

## Slide 56: QoS Overview
Quality of Service (QoS) defines a service provider's ability to guarantee a certain level of performance required by customers. The QoS-enabled device controls enterprise network traffic, implements congestion management and congestion avoidance, reduces the packet loss rate, and provides dedicated bandwidth for enterprise users or differentiated services (such as audio, video, and data services).
Video traffic
Audio traffic
Data traffic
Inbound interface
Traffic classification
Token bucket
Token
Remark
Other processing methods
...
Queue 0
Queue 1
Queue 2
Queue N
...
GTS
WRED
Congestion avoidance
Packet enqueuing
Scheduling
Congestion management
Traffic shaping
Traffic policing
Outbound interface
Leaving queues
CAR
QoS implementation
Notes: To meet SLA requirements of different services (such as audio, video, and data services), the network is required to distinguish different communication modes before providing corresponding QoS guarantee.
  For example, real-time services such as voice over IP (VoIP) demand a shorter delay. A long delay for packet transmission is unacceptable. Email and File Transfer Protocol (FTP) services are comparatively insensitive to the delay.
  Conventional IP networks provide the best-effect mode, which cannot help identify or differentiate the communication types on the network. The capability of differentiating communication types is the prerequisite for providing differentiated services. Therefore, the best-effect mode cannot meet the requirements of the emerging applications. This is where QoS comes in.
QoS is designed to provide differentiated services based on application requirements. For example:
  The bandwidth used by the FTP service on the backbone network can be limited, and a higher priority can be assigned to database access.

## Slide 57
Notes:   An Internet service provider (ISP) can transmit real-time services such as audio or video services. With QoS technology, the ISP can differentiate the packets and provide differentiated services for users.
  High bandwidth and short delays can be guaranteed for the time-sensitive multimedia services. If other services are available on the network, these time-sensitive services are not affected.

## Slide 58: QoS Application Example
In the enterprise WAN interconnection scenario, QoS is typically deployed on the egress link.
QoS technology is used to ensure high network bandwidth and short delays for high-value services.
Video stream
Audio stream
Data stream
Video
Audio
Data
LAN
WAN
LAN
QoS is deployed in the outbound direction of the interface to rate-limit traffic and preferentially schedule high-priority traffic.
Application scenario of QoS

## Slide 59: Overview of HQoS
Conventional QoS schedules traffic based on interfaces. Interfaces themselves can only differentiate service priorities. Traffic of the same priority uses the same interface queue and compete for the same queue resources. Therefore, conventional QoS is unable to provide differentiated services based on the types of traffic and users.
HQoS implements hierarchical scheduling based on multiple levels of queues, differentiating both services and users to provide fine-tuned QoS guarantee.
In home broadband scenarios, different families may lease different network bandwidths and network services. QoS cannot be used to implement fine-tuned management of these families.
QoS limitations in multi-tenant scenarios
Internet
Three tenants: 20 Mbit/s bandwidth, HSI service
Three tenants: 30 Mbit/s bandwidth, IPTV service
Two tenants: 50 Mbit/s bandwidth, VoIP service
Three tenants: 20 Mbit/s bandwidth, IPTV service
Three tenants: 50 Mbit/s bandwidth, VoIP service
User-based QoS cannot be implemented at the egress, and up to eight queues can be used to differentiate traffic.
14 families rent different network bandwidths and services.

## Slide 60: HQoS Application Example
HQoS is mainly used in multi-tenant scenarios. For example, there are three families in a building. Family A has purchased 10 Mbit/s bandwidth and subscribed to VoIP, IPTV, and HSI services. Family B has purchased 20 Mbit/s bandwidth and subscribed to IPTV and HSI services. Family C has purchased 30 Mbit/s bandwidth and subscribed to the HSI service. These three families have different requirements. HQoS is the best choice for this scenario.
Total bandwidth of the building: 60 Mbit/s
Total bandwidth of family A: 10 Mbit/s
Total bandwidth of family B: 20 Mbit/s
Family A
Family B
Family C
Deploy HQoS at the egress
HQoS application example
VoIP (PQ scheduling)
IPTV (PQ scheduling)
HSI (WFQ scheduling)
IPTV (PQ scheduling)
HSI (WFQ scheduling)
HSI (WFQ scheduling)
WFQ
Level 3 flow queue
Level 2 subscriber queue
Level 1 port queue
Total bandwidth of family C: 30 Mbit/s
Notes: VoIP: voice over IP service
IPTV: Internet protocol TV service
HSI: high-speed Internet service

## Slide 61
Basic Architecture of a Typical WAN Interconnection Solution
Networking Technologies and Their Applications of WAN Interconnection
Reliability Technologies and Their Applications of WAN Interconnection
Optimization Technologies and Their Applications of WAN Interconnection
  QoS Technology and Its Application
  FEC Technology and Its Application

## Slide 62: Overview of FEC
An IP video call often encounters image distortion or audio interruption due to packet loss. To prevent this, error control technologies are required.
Forward error correction (FEC) is such a technology. The sender attaches FEC redundant packets to the data to be transmitted. If an error is detected, the receiver can correct the data based on the redundant packets.
FEC is applicable to networks where random packet loss occurs or the RTT is large.
MPLS
Internet
1
2
3
4
Key traffic
1
2
3
4
Key traffic
Add FEC redundant packets
P
Data packet loss
1
3
4
Key traffic
P
2
FEC restoration
FEC implementation
Notes: Error control technologies are classified into forward error correction (FEC) and backward error correction (BEC).
  Automatic repeat request (ARQ) is an on-demand retransmission mechanism. The sender uses a "sending-acknowledgement" mechanism to detect whether the receiver receives data packets. If the sender does not receive any acknowledgment packet from the receiver, the sender retransmits the corresponding packet. In this error correction mode, packets need to be sent repeatedly. As a result, an extra delay is introduced. In this mode, the sender retransmits packets to implement error correction. This is why this mode is called BEC.
  In FEC, both FEC redundant packets and data packets are sent to the receiver. If an error is found, the receiver directly restores the lost data packets by using the FEC redundant packets. In this mode, error correction is performed on the receiver. This is why this mode is called FEC.
    The error correction capability of FEC is limited. For example, if three out of four packets are lost, FEC cannot restore these three packets based on the remaining packet.

## Slide 63: Overview of A-FEC
In terms of FEC, the ratio of the original data to FEC redundant packets is fixed. If burst packet loss occurs, the original data may fail to be restored based on the redundant packets. Considering this, FEC is not applicable to the network where burst packet loss may occur. In addition, since FEC will add redundant packets, the bandwidth utilization will decrease. This is where adaptive-FEC (A-FEC) technology comes in.
A-FEC technology can flexibly add redundant packets based on the live network quality.
  When the network quality is good, A-FEC adds a few redundant packets or even does not add any redundant packet to improve bandwidth utilization.
  When the network quality is poor, A-FEC adds more redundant packets to prevent data restoration failures caused by burst packet loss.
MPLS
Internet
1
3
4
Add a few FEC redundant packets.
P
2
Good network quality
Poor network quality
1
3
4
Add a large number of FEC redundant packets.
P
2
P

## Slide 64: Exemplary Application Scenario of FEC/A-FEC
FEC or A-FEC can be used to guarantee mission-critical video applications and reduce frame freezing and artifacts.
Application scenario of FEC or A-FEC
The A-FEC algorithm is used to flexibly increase redundant packets at the transmit end based on the application and link quality to prevent continuous packet loss on the network. This helps prevent mission-critical video applications from frame freezing or artifacts even when the packet loss rate reaches up to 20%.
MPLS
Internet
1
3
4
Add a few FEC redundant packets.
P
2
Good network quality
Poor network quality
1
3
4
Add a large number of FEC redundant packets.
P
2
P
Video server
Multimedia terminal

## Slide 65
(Multiple-answer question) Which of the following are private line technologies? ( )
  SDH
  L2TP
  MPLS VPN
  IPsec VPN
(True or false) SRP technology can flexibly select egress links based on the link quality. ( )
  True
  False
Notes: AC
A

## Slide 66
There are two WAN interconnection modes: private line and VPN.
To ensure WAN reliability, the link quality needs to be detected first, and then specific technologies are used to select a proper egress or egress link based on the link quality.
There are many WAN optimization methods. Typically, QoS is used to control egress traffic and FEC is used to ensure reliable data forwarding on WANs.