## Slide 1
Datacom
General
V1.0
Wu Yue/WX291773
2021.9.20
He Junjian/WX580230
New

## Slide 2: Key Technologies of WAN Interconnection

## Slide 3
Wide area interconnection technologies are diverse, and different technologies have different application scenarios and backgrounds.
On the live network, GRE and L2TP are used as WAN interconnection technologies. To ensure the security of GRE and L2TP tunnels, IPsec is used as an auxiliary technology.
On the live network, some WAN interconnection devices are located behind NAT devices. Therefore, NAT traversal can be used in many WAN interconnection scenarios.
To ensure WAN interconnection reliability, multiple links are generally deployed in the uplink. Multi-link routing is also an important WAN interconnection technology.
This course describes common technologies used in WAN interconnection scenarios.

## Slide 4
On completion of this course, you will be able to:
  Describe the working principles of common WAN interconnection technologies.
  Describe the working principles of IPsec.
  Describe the common solutions and basic principles of NAT traversal.
  Describe how Wide Area Interconnect intelligent traffic steering works

## Slide 5
Common Networking Technologies in WAN Interconnection
  GRE Fundamentals and Application Scenarios
  L2TP Fundamentals and Application Scenarios
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 6: GRE Background
With the development of enterprises, more and more enterprises need to communicate between branches and headquarters. Private lines (such as MPLS and SDH/MSTP private lines) need to be leased for communication between the headquarters and branches. However, private lines are expensive. For small- and medium-sized enterprises or cross-border companies, the cost is high.
With the development of the Internet, the Internet has sufficient bandwidth and coverage. Therefore, it is more feasible to implement communication on the intranet between the headquarters and branches through the Internet. GRE is proposed in this background.
Internet
Branch site
Branch site
HQ
Branch site
Interconnection between branches and HQ
Internet
GRE tunnel
GRE tunnel
GRE tunnel
Through GRE tunnels, the enterprise network can be established between the branch and headquarters based on the Internet.
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 7: Introduction to Tunneling Technologies
GRE is one of tunneling technologies. A tunnel is similar to a bridge. Forwarding channels are established on the underlying network (for example, Internet). Users can establish a tunnel network by themselves without the intervention of the underlying network provider (for example, an ISP).
There are many tunneling technologies, such as MPLS, GRE, Layer 2 Tunneling Protocol (L2TP), and Virtual Extensible LAN (VXLAN). The following figure shows the implementation of tunnel data forwarding.
Branch
HQ
Internet
Inner Header
Data
Outer Header
Inner Header
Data
Inner Header
Data
Encapsulate the outer header
Inner Header
Data
Outer Header
The device forwards the packet on the underlying network based on the outer header. The underlying network is unaware of the inner data.
Decapsulate the outer header
Inner Header
Data
Inner Header
Data
Tunnel
Implementation of tunnel data forwarding
Tunnel data forwarding
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 8: Basic Concepts of GRE
As a Layer 3 tunneling technology, GRE encapsulates packets of a protocol into packets of another protocol to transparently transmit packets over GRE tunnels. This technology enables packet transmission between the HQ and branches.
GRE tunnels can transmit IPv4/IPv6 unicast, multicast, and broadcast packets.
GRE packet format:
L2 Header | New IP Header | GRE Header | Raw IP Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
32 bits
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
Notes: Description of fields in a GRE header:
Field | Description
C | Checksum verification bit. The value 1 indicates that the Checksum field is inserted into the GRE header. The value 0 indicates that the GRE header does not contain the checksum field.
K | Key bit. The value 1 indicates that the Key field is inserted into the GRE header. The value 0 indicates that the GRE header does not contain the keyword field.
Recursion | Number of layers where GRE packets are encapsulated. The value of this field is increased by 1 after one GRE encapsulation is complete. If the number of encapsulation layers is greater than 3, the packet is discarded. This field is used to prevent packets from being encapsulated continuously.
Flags | Reserved field. The value must be 0.
Version | Version. The value must be 0.
Protocol Type | Type of the passenger protocol. A common passenger protocol is the IPv4 protocol, with the value of 0800. The protocol number of Ethernet over GRE is 0x6558.
Checksum | Checksum of the GRE header and the payload.
Key | Key used to authenticate the packet at the receive end.

## Slide 9: GRE Fundamentals
The GRE tunnel is a Layer 3 tunnel and mainly carries IPv4/IPv6 packets. GRE encapsulates the outer IP header so that data can be transmitted on the public network. In this way, enterprise branches and the headquarters can communicate with each other.
The following figure shows the process of forwarding packets over a GRE tunnel.
Branch
HQ
Encapsulate the outer header
The device forwards the packet on the underlying network based on the outer IP header.
Decapsulate the outer header
GRE tunnel
S: IP1, D: IP2
Data
S: IP1, D: IP2
Data
GRE
S: IPA, D: IPB
GRE tunnel interface
GRE tunnel interface
IP1
IP2
IPA
IPB
S:IP1，D:IP2
Data
GRE
S: IPA, D: IPB
S: IP1, D: IP2
Data
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 10: Keepalive Detection
The current GRE protocol does not have the link status detection function. If the remote interface is unreachable, the GRE tunnel cannot be terminated immediately. As a result, the source continuously forwards packets to the peer. The peer, however, cannot receive packets because the tunnel is unreachable. In this case, traffic is interrupted.
The keepalive detection function monitors tunnel status to check whether the remote end is reachable.
Keepalive timeout interval = Sending interval (5s by default) x Retry count (3 by default)
GRE tunnel
GRE Keepalive
Timeout timer
GRE Keepalive
Reply with a keepalive message within the timeout interval.
The keepalive message does not expire and the tunnel status is normal.
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
Notes: Keepalive detection functions as follows:
  After being enabled on the source end of a GRE tunnel, the source end starts a timer to periodically send and count keepalive messages. The number of sent keepalive messages increases by one each time a keepalive message is sent.
  The destination end sends a response message to the source end each time it receives a keepalive message from the source end.
  If the source end receives a reply packet before the counter value reaches the preset value, it considers the remote end reachable. If the source end does not receive any response message before the counter reaches the preset value, specifically, the retry count, the source end considers the peer end unreachable and resets the counter. Then, the source end terminates the tunnel connection. In this case, the source interface still sends Keepalive messages to the remote interface. When the remote interface becomes Up, the source interface becomes Up and sets up a tunnel with the remote interface.

## Slide 11: Security Threats to GRE Tunnels
GRE tunnels are used to transmit data between branches and the HQ. Data is not encrypted and may be tampered with.
There are potential risks in GRE tunnel establishment. Attackers can forge IP addresses to establish GRE tunnels between authorized and unauthorized devices.
GRE data tampering
GRE tunnel
Data tampering
Unauthorized GRE tunnel setup
GRE tunnel
Unauthorized GRE tunnel
GRE
Outer Header
Payload
GRE
Outer Header
Payload
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 12: GRE Data Check and Verification
Checksum verification is an end-to-end check on encapsulated packets.
If the C bit in the GRE header is set to 1, the checksum is valid. The sender calculates the checksum based on the GRE header and payload. Then it sends out the packet that carries the checksum. After receiving the packet, the receiver also calculates the checksum and compares the result with the checksum carried in the packet. If they are the same, the receiver further processes the packet. Otherwise, it discards the packet.
Outer Header | GRE Header | Inner Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
Data verification used to prevent data tampering
GRE tunnel
Payload
Data tampering
GRE
Payload
GRE
Outer Header
C=1,Checksum=A
C=1,Checksum=B
Verification fails and data is discarded.
Inconsistent checksum
Outer Header
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
Notes: You can enable or disable checksum verification on both ends of a tunnel in actual applications. If checksum verification is enabled on the local end and disabled on the remote end, the local end does not check checksum values of received packets, but checks checksum values of packets to be sent. If checksum verification is disabled on the local end and enabled on the remote end, the local end checks checksum values of received packets, but does not check checksum values of packets to be sent.

## Slide 13: GRE Key
Key authentication is used to verify validity of a tunnel interface. This security mechanism prevents tunnel interfaces on two devices at both ends of a GRE tunnel from incorrectly identifying and receiving packets from other devices.
If the K bit in the GRE header is set to 1, a four-byte Key field is inserted into the GRE header. Both the receiver and the sender need to authenticate the key.
GRE tunnel
Unauthorized GRE tunnel
GRE Key=10
GRE Key=10
GRE Key=20
The tunnel cannot be established because the keys are inconsistent.
The GRE key is used to prevent unauthorized GRE tunnel establishment.
Outer Header | GRE Header | Inner Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
Notes: This field identifies traffic in a tunnel. Packets of the same traffic use the same key. During packet decapsulation, GRE identifies data packets of the same traffic based on the key. Packets will pass verification only when the two ends of the tunnel use the same Key field. If packets fail the verification, they will be discarded. Successful authentication requires that both ends are either configured with the same Key field or not configured with the Key field.

## Slide 14: Using GRE to Build an Intranet Between the HQ and Branches
GRE tunnels can transmit IPv4/IPv6 unicast, multicast, and broadcast packets. Dynamic routing neighbor relationships can be configured between branches and the HQ through GRE tunnels, facilitating intranet interconnection between branches and the HQ.
GRE tunnel
Branch 1
HQ
Branch 2
GRE tunnel
OSPF area 1
OSPF area 2
OSPF area 0
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 15: GRE Over IPsec
GRE is simple. However, data is transmitted over a GRE tunnel in cleartext and can be easily obtained. On the live network, GRE is usually used together with IPsec. The GRE technology is used to establish the internal network connection between the branch and headquarters, and the IPsec technology is used to encrypt GRE tunnel packets.
GRE over IPsec data encapsulation
Internet
IPsec tunnel
IPsec tunnel
GRE tunnel
IP data
IPsec data
IP data
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 16: Limitations of MPLS VPN Networking
To connect a CE to an MPLS VPN, you must use a physical link to directly connect the CE to a PE on the MPLS backbone network.
In actual networking, however, not all CEs and PEs can be directly connected through physical links. For example, for multiple organizations that connect to the Internet or IP backbone network, their CEs may be far away from the PEs on the MPLS backbone network; therefore, they cannot be connected directly. Devices in these organizations cannot directly access the internal sites of the MPLS VPNs through the Internet or IP backbone network.
Internet
MPLS
Branch1
VPN1
VPN2
Branch2
Branch egress
Branch egress
DC1 egress
DC2 egress
Branch aggregation
PE
PE
PE
Indirectly connected link
The VPN to which traffic belongs cannot be identified.
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 17: Connecting to the MPLS VPN Through GRE Tunnels
To enable a CE to access the MPLS VPN and ensure data transmission security, you can connect the CE and a PE through a public or private network, create a GRE tunnel between the CE and the PE, and associate the VPN with the GRE tunnel interface on the PE.
Internet
MPLS
Branch1
VPN1
VPN2
Branch2
Branch egress
Branch egress
DC1 egress
DC2 egress
Branch aggregation
PE
PE
GRE tunnel
GRE tunnel
MPLS VPN tunnel
MPLS VPN tunnel
VRF1
VRF2
GRE tunnel
GRE tunnel
MPLS VPN tunnel
MPLS VPN tunnel
PE
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios

## Slide 18
Common Networking Technologies in WAN Interconnection
  GRE Fundamentals and Application Scenarios
  L2TP Fundamentals and Application Scenarios
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 19: L2TP Overview
By combining the advantages of the Layer 2 Forwarding (L2F) and Point-to-Point Tunneling Protocol (PPTP), Layer 2 Tunneling Protocol (L2TP) is an industry standard defined by the IETF. L2TP is a virtual private dialup network (VPDN) tunneling protocol that extends Point-to-Point Protocol (PPP) applications. It is an important VPN technology that provides access services for employees on the go to remotely access intranet resources.
Fundamentals
Application Scenarios

## Slide 20: Basic Architecture of L2TP
NAS
  A network access server (NAS) is maintained by an ISP and connects to a dialup network.
LAC
  An L2TP access concentrator (LAC) provides PPP and L2TP processing capabilities on a packet switched network.
LNS
  An L2TP network server (LNS) is the peer device of an LAC. That is, an L2TP tunnel is established between them.
Tunnel and session
  An L2TP tunnel is established between an LAC and an LNS. Multiple L2TP tunnels can be established between an LAC and an LNS, and an L2TP tunnel can contain multiple L2TP sessions.
Enterprise branch
Dialup network
LNS
NAS
(LAC)
Client
(LAC)
L2TP client
(LAC)
HQ
L2TP tunnel
PPP terminal
L2TP session
Fundamentals
Application Scenarios
Notes: NAS
  A network access server (NAS) is maintained by an ISP and connects to a dialup network. It is the nearest access point for PPP terminals. An NAS is used on a traditional dialup network. An ISP deploys an LAC on an NAS to provide L2TP services for remote dialup users and to establish tunnel connections with the enterprise headquarters.
LAC
  An L2TP access concentrator (LAC) provides PPP and L2TP processing capabilities on a packet switched network. An LAC establishes an L2TP tunnel connection with an L2TP network server (LNS) based on the user name or domain name carried in PPP packets to extend PPP negotiation to the LNS. Different networking environments can have different devices functioning as an LAC.
    NAS-initiated scenario: On a traditional dialup network, an ISP deploys an LAC on an NAS. Alternatively, on the Ethernet of an enterprise branch, the ISP deploys a gateway for PPP terminals. The gateway functions as both a PPPoE server and an LAC.
    L2TP client-initiated scenario: In an enterprise branch, an L2TP client functioning as an LAC is configured on the gateway to initiate an L2TP tunnel establishment request to an LNS. In this case, no dialup is required in the remote system to trigger L2TP tunnel establishment.
    Client-initiated scenario: An employee on the go uses a PC or mobile terminal to access the Internet and uses the L2TP dialup software on the PC or mobile terminal. In this scenario, the PC or mobile terminal functions as an LAC.
  An LAC can establish multiple L2TP tunnels to isolate data flows. That is, it can carry multiple L2TP connections.

## Slide 21
Notes: LNS
  An LNS terminates PPP sessions. After being authenticated by the LNS, remote users successfully set up PPP sessions with the LNS and can access resources in the enterprise headquarters. For L2TP negotiation, the LNS is the peer device of the LAC. That is, an L2TP tunnel is established between the LAC and the LNS. For PPP, the LNS is the logical endpoint of a PPP session. That is, a point-to-point virtual link is set up between the PPP terminal and the LNS.
  An LNS, located at the border between the enterprise headquarters' private network and the public network, is usually a gateway of the enterprise headquarters. If necessary, the LNS also provides the network address translation (NAT) function to translate private IP addresses on the enterprise headquarters network into public IP addresses.

## Slide 22: Message Structure of L2TP
L2TP contains two types of messages: control messages and data messages.
  Control messages are used to establish, maintain, and tear down L2TP tunnels and sessions.
  Data messages encapsulate PPP data frames and are transmitted over L2TP tunnels.
Control message structure
Data message structure
Enterprise branch
Enterprise HQ
Dialup network
NAS (LAC)
LNS
IP packet
Original IP Header | UDP Header | L2TP Header | L2TP Control Data
New IP Header | UDP Header | L2TP Header | PPP Header | Original IP Header | Traffic Data
PPP encapsulation
L2TP encapsulation
Fundamentals
Application Scenarios
Notes: Control message
  Control messages are used to establish, maintain, and tear down L2TP tunnels and sessions. During the transmission of control messages, mechanisms such as retransmission of lost messages and periodic detection of tunnel connectivity are used to ensure the reliability of control message transmission. Traffic control and congestion control on control messages are supported.
  Control messages are transmitted over an L2TP control channel. The control channel encapsulates control messages with L2TP headers and transmits them over an IP network.
Data message
  Data messages are used to encapsulate PPP frames, which are transmitted over tunnels, but such tunnels are unreliable. That is, a lost data message is not retransmitted, and traffic control and congestion control on data messages are not supported.
  Data messages carrying PPP frames are transmitted over unreliable data channels. PPP frames are encapsulated using L2TP and then transmitted over the IP network.

## Slide 23: Working Process of L2TP
L2TP can be used to transmit data. The working process of L2TP is as follows:
  Establishing an L2TP tunnel
  Establishing an L2TP session
  Transmitting PPP packets
Enterprise branch
Enterprise HQ
Dialup network
NAS (LAC)
LNS
1. Call connection setup
2. PPP LCP negotiation
3. PAP/CHAP authentication
4. Authentication result
RADIUS server
RADIUS server
DNS server
5. LNS IP address resolution
6. L2TP tunnel establishment
7. L2TP session establishment
8. PPP negotiation message
9. (Optional) CHAP re-authentication
10. Authentication result
11. IP address allocation after a successful L2TP connection
12. Communication between the enterprise branch and headquarters
Fundamentals
Application Scenarios
Notes: Establishing an L2TP tunnel
  After receiving a PPP negotiation request from a remote user, the LAC sends an L2TP tunnel establishment request to the LNS. The LAC and the LNS exchange L2TP control messages to negotiate the tunnel ID and tunnel authentication information. After the negotiation succeeds, an L2TP tunnel is established between them and identified by the tunnel ID.
Establishing an L2TP session
  If an L2TP tunnel exists, the LAC and the LNS exchange control messages to negotiate the session ID. If no L2TP tunnel exists, the LAC and the LNS establish an L2TP tunnel first. The L2TP session carries LCP negotiation information and user authentication information of the LAC. After authenticating such information, the LNS notifies the LAC of the session establishment. The L2TP session is identified by a session ID.
Transmitting PPP packets
  After the L2TP session is established, the PPP terminal sends data packets to the LAC. The LAC encapsulates the L2TP packets based on information such as the L2TP tunnel and session ID and sends the packets to the LNS. The LNS decapsulates the L2TP packets and sends the packets to the destination host based on the routing and forwarding table.

## Slide 24: Mobile Office
Employees on the go connect to the intranet through L2TP. The LNS can authenticate access users and assign private IP addresses to them. If ACLs are configured, the LNS can also manage access rights of access users.
Employee on the go
(L2TP software)
LNS
PC
Enterprise HQ
L2TP encapsulation
Fundamentals
Application Scenarios
Notes: Employees on the go may need to communicate with the headquarters and access intranet resources of the headquarters at any time. Although they can access the headquarters gateway through the Internet, the headquarters gateway cannot identify and manage access users. To address this issue, configure the headquarters gateway as an LNS, so that virtual point-to-point connections can be established between the employees on the go and the headquarters gateway when the employees use the L2TP dialup software on the PC to initiate L2TP connections.

## Slide 25: Interconnection Between Branches and the Headquarters
An enterprise sets up a VPN to connect its branch network to its headquarters network. After IP packets from branch users reach the L2TP client, the L2TP client forwards the packets to the virtual dialup interface. The virtual dialup interface forwards the packets to the LNS, which then forwards the packets to the destination host.
PC
Enterprise branch
Enterprise HQ
PC
L2TP encapsulation
L2TP client
LNS
Fundamentals
Application Scenarios
Notes: An enterprise has some branches located in other cities, and its branches use the Ethernet and have gateways deployed for branch users to access the Internet. The headquarters provides access services for branches. VPDN connections need to be established between branches and the headquarters gateway. Any branch user is allowed to access the headquarters network, and only the branch gateways need to be authenticated. In this case, the headquarters gateway functions as the LNS, and the branch gateways function as the L2TP clients. Virtual dialup is created on the branch gateways to trigger L2TP tunnel connections to the headquarters network. A virtual point-to-point connection is established between an L2TP client and the LNS. After IP packets of branch users reach an L2TP client, the L2TP client forwards the packets to the virtual dialup interface. The virtual dialup interface forwards the packets to the LNS, which then forwards the packets to the destination host.

## Slide 26: Interconnection Between Employees in Branches and the Headquarters
Branch employees use PPPoE dialup software to connect to the headquarters network, and the branch gateway functions as the PPPoE server and LAC to forward call requests from branch users to the headquarters network.
PPP terminal
(PPPoE client)
Enterprise branch
Enterprise HQ
PC
L2TP encapsulation
L2TP client
LNS
PPPoE
Fundamentals
Application Scenarios
Notes: An enterprise has some branches located in other cities, and its branches use the Ethernet and have gateways deployed for branch users to access the Internet. Headquarters users need to communicate with branch users, and the headquarters uniformly manages access of branch users. Therefore, L2TP is used to deploy the headquarters gateway as an LNS. Dialup packets of branch users cannot be transmitted directly over the Ethernet. Therefore, PPPoE dialup software needs to be deployed as a PPPoE client on the terminal that initiates the dialup packets, and the branch gateway functions as a PPPoE server and an LAC to forward call requests of branch users to the headquarters.

## Slide 27
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
  Basic Concepts of IPsec
  IPsec Fundamentals
  IPsec Application Scenarios
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 28: IPsec Background
Enterprise branches often need to communicate with each other. They can communicate using many methods, for example, using private lines or Internet links.
Considering costs and requirements, some enterprises choose to use Internet links for interconnection. However, data may be intercepted when being transmitted on the Internet, posing security risks.
IPsec technology encrypts data packets to secure enterprise interconnections.
Carrier network
Branch site
Branch site
HQ
Branch site
Enterprise WAN interconnection
WAN
IPsec tunnel
IPsec tunnel
IPsec tunnel
IPsec Overview
IPsec Framework

## Slide 29: IPsec Overview
On the live network, GRE over IPsec technology is typically used for interconnection between branch sites. IPsec technology ensures secure data transmission, and GRE technology ensures interconnection between enterprise intranets.
The IPsec protocol suite is a series of security protocols developed by the Internet Engineering Task Force (IETF). It provides a cryptology-based, interoperable, and high-quality security protection mechanism for end-to-end IP packet exchange.
IPsec encrypts and authenticates data to ensure secure data transmission on the Internet.
IPsec VPN technology can be used with multiple VPN technologies to provide flexible and secure enterprise interconnections.
Enterprise egress
HQ
Enterprise branch
Carrier network
Enterprise egress
Data encryption and authentication
Data encryption and authentication
Data is encrypted
IPsec tunnel
GRE tunnel
GRE over IPsec
IPsec tunnel
IPsec Overview
IPsec Framework

## Slide 30: Data Encryption
Data encryption prevents data from being leaked during data forwarding. Two data encryption methods are available:
  Symmetric encryption: The same password is used for encryption and decryption, which is highly efficient. However, the key may be intercepted during key exchange.
  Asymmetric encryption: The public key is used for encryption and the private key is used for decryption. Data security is high but the data encryption and decryption efficiency is low.
Symmetric encryption
Data
Data
Key A
Key A
The same key is preconfigured or transmitted in advance
Encrypted data
Encrypted data
Data forwarding
RT1
RT2
Asymmetric encryption
Data
Data
Public key B
Private key B
Encrypted data
Encrypted data
Data forwarding
RT1
RT2
Encryption
Decryption
Public key encryption
Private key decryption
Public key B
Private key B
Key pair
The device automatically generates a public key and a private key
Public key transmission
Key exchange
IPsec Overview
IPsec Framework
Notes: The symmetric encryption algorithm is also called traditional cryptographic algorithm, in which the encryption key can be calculated from the decryption key. The sender and receiver share the same key, which is used for both encryption and decryption. Symmetric key encryption is an effective method for encrypting a large amount of data. There are many algorithms for symmetric key encryption, and all of them aim to convert between cleartext (unencrypted data) and ciphertext. Because symmetric key encryption uses the same key for data encryption and decryption, data security depends on whether unauthorized users obtain the symmetric key. If two communicating parties want to use the symmetric key to encrypt data, they must exchange the key securely before exchanging the encrypted data.
An asymmetric algorithm is also called public key algorithm, in which a public key is used for encryption and a private key for decryption. The two keys are mathematically related. In public key encryption, the public key can be publicly transmitted between two communicating parties or released in the public repository, but the private key is confidential. The data encrypted using the public key can be decrypted only using the private key. The data encrypted using the private key can be decrypted only using the public key.

## Slide 31: Data Authentication
The main purpose of data authentication is to check whether data is tampered with. Data authentication is mainly based on the hash algorithm.
  A unique hash value is calculated based on the hash algorithm and then carried in the data before being forwarded to the peer device.
  The peer device hashes the data again to obtain the hash value. It then compares the received hash value with the calculated one. If they are the same, the data is not tampered with.
Hash algorithm
Hash algorithm
Data forwarding
RT1
RT2
Hash calculation
Hash calculation
Data
Hash value A
Data
Hash value A
Hash value B
Compare hash values
IPsec Overview
IPsec Framework

## Slide 32: IPsec Encryption
IPsec uses both symmetric encryption and asymmetric encryption, ensuring data security and performance.
  Uses an asymmetric algorithm to encrypt and transmit the key used for symmetric encryption.
  Uses the exchanged symmetric key to encrypt data.
IPsec encryption and decryption
IPsec device
IPsec device
Asymmetric encryption
Symmetric key
Symmetric key
Asymmetric encryption
User data
User data
Symmetric encryption
Symmetric encryption
Exchange the symmetric key
Use the public key to encrypt data
Use the private key to decrypt data
Use the public key to encrypt data
Use the private key to decrypt data
Exchange user data
Encrypt and decrypt data using the symmetric key
Encrypt and decrypt data using the symmetric key
IPsec tunnel
After the symmetric key is exchanged, the symmetric key is used to encrypt and decrypt data.
1
2
IPsec Overview
IPsec Framework

## Slide 33: SA
A security association (SA) is an agreement between two IPsec peers on certain elements. For example, Data Encryption Standard (DES) is used as the encryption algorithm, Message Digest Algorithm 5 (MD5) is used as the authentication algorithm, and tunnel is used as the encapsulation mode.
An IPsec SA can be established manually or through Internet Key Exchange (IKE) negotiation.
Establishing IPsec SAs through IKE negotiation
IKE
module
IKE
module
IKE SA negotiation
Authentication policy 1
Encryption policy 1
Key 1
...
Authentication and encryption policy 1
Key 1
...
Unified encryption and authentication elements after negotiation
IPsec SA negotiation
Authentication policy 2
Encryption policy 2
Key 2
...
Establishing IPsec SAs manually
Manual configuration
Authentication policy 1
Encryption policy 1
Key 1
...
Authentication policy 1
Encryption policy 1
Key 1
...
IPsec SA
IPsec Overview
IPsec Framework
Notes: IPsec technology supports multiple data encryption, authentication, and encapsulation algorithms. When devices at both ends use IPsec for secure communication, they must use the same encryption and authentication algorithms. Therefore, a mechanism is required to help the devices negotiate these parameters.
An IPsec SA can be established in either of the following ways:
  Manual configuration: The management cost of manually established IPsec SAs is high. This is because the encryption and authentication modes need to be manually configured, SAs need to be manually updated, and SA information permanently exists, resulting in low security. This mode applies to small-scale networks.
  IKE negotiation: The management cost of IPsec SAs established through IKE negotiation is low. The encryption and authentication modes are generated using the Diffie-Hellman (DH) algorithm, SA information is generated periodically, and SAs are dynamically updated. This mode applies to small-, medium-, and large-sized networks.
An SA is uniquely identified by three parameters: security parameter index (SPI), destination IP address, and security protocol ID (AH or ESP).
An IKE SA is used to establish a secure channel for exchanging IPsec SAs.

## Slide 34: Key Exchange
On the live network, the Internet Key Exchange (IKE) protocol is typically used to exchange symmetric keys.
IKE is a UDP-based application-layer protocol. It is built upon the framework defined by the Internet Security Association and Key Management Protocol (ISAKMP). IPsec uses IKE for key auto-negotiation and IPsec SA establishment, simplifying IPsec configuration and maintenance.
IKE using ISAKMP for SA exchange
IPsec device
IPsec tunnel
IPsec device
IKE module
SA negotiation
IKE module
IP Header
ISAKMP Data
UDP:500
IP Header
ISAKMP Data
UDP:500
The IKE module exchanges SA information through ISAKMP messages.
IPsec Overview
IPsec Framework
Notes: IKE supports the following authentication algorithms including MD5, Secure Hash Algorithm 1 (SHA1), SHA2-256, SHA2-384, SHA2-512, and Senior Middle 3 (SM3).
IKE supports the following encryption algorithms: DES, 3DES, AES-128, AES-192, AES-256, SM1, and SM4.
ISAKMP is defined in RFC 2408, which defines the procedures for negotiating, establishing, modifying, and deleting SAs and defines the ISAKMP message format. ISAKMP provides a general framework for SA attributes and the methods of negotiating, modifying, and deleting SAs, without defining the specific SA format.
ISAKMP messages can be transmitted using UDP or TCP through port 500. In most cases, ISAKMP messages are transmitted using UDP.

## Slide 35: Data Encryption and Authentication
IPsec provides two security mechanisms: authentication and encryption.
  IPsec uses symmetric encryption algorithms to encrypt and decrypt data. These algorithms require that the sender and receiver use the same key (a symmetric key) to encrypt and decrypt data.
  IPsec uses the Hash-based Message Authentication Code (HMAC) function to compare digital signatures to check data integrity and authenticity.
Data encryption, decryption, and authentication
User packet
Encryption algorithm (encryption)
Encrypted packet
User packet
Encryption algorithm (decryption)
Encrypted packet
Symmetric key exchange
Manually configured or automatically negotiated through IKE
Authentication algorithm (HMAC)
Authentication algorithm (HMAC)
Encrypted packet
ICV
ICV
Encrypted packet
ICV
Whether they are consistent
Discard
No
Yes
IPsec Overview
IPsec Framework
Symmetric key exchange
Manually configured or automatically negotiated through IKE
Notes: Integrity check value (ICV) is used by the receiver for integrity check. Available authentication algorithms are MD5, SHA1, SHA2, and SM3.
Common symmetric encryption algorithms used by IPsec include Data Encryption Standard (DES), Triple Data Encryption Standard (3DES), Advanced Encryption Standard (AES), and algorithms approved by State Cryptography Administration, such as SM1 and SM4. DES and 3DES are not recommended because they are insecure and pose security risks.
Common authentication algorithms used by IPsec include MD5, SHA1, SHA2, and SM3. MD5 and SHA1 are not recommended because they are insecure and pose security risks.
IPsec encryption cannot verify the authenticity or integrity of information after decryption. IPsec uses the HMAC function to compare digital signatures to check integrity and authenticity of data packets. In most cases, encryption and authentication are used together. The IPsec sender uses the authentication algorithm and symmetric key to generate a digital signature for the encrypted packet and sends the IP packet and digital signature to the receiver. The receiver uses the same authentication algorithm and symmetric key to process the encrypted packet and then generates a digital signature. Then the receiver compares the received and generated digital signatures to verify the data integrity and authenticity. If the packet passes the verification, the receiver decrypts it. Otherwise, the receiver discards it.

## Slide 36: Security Protocols
IPsec provides two transport layer protocols for authentication or encryption: Authentication Header (AH) and Encapsulating Security Payload (ESP).
  AH provides only authentication but no encryption capabilities.
  ESP provides both authentication and encryption.
AH header format
ESP header format
Next Header | Payload Len | Reserved
Security Parameters Index (SPI) |  | 
Sequence Number |  | 
Authentication Data (Variable) Integrity Check Value (ICV) |  | 
32 bits
Security Parameters Index (SPI) |  |  | 
Sequence Number |  |  | 
Payload Data (Variable) |  |  | 
 | Padding (0-255 Octets) |  | 
 |  | Pad Len | Next Header
Authentication Data (Variable) Integrity Check Value (ICV) |  |  | 
32 bits
ESP
Header
ESP
Trailer
Encrypted
ESP
Authentication
Authentication
IPsec Overview
IPsec Framework
Notes: AH provides only authentication but no encryption capabilities. According to the AH protocol, an AH header is appended to the standard IP header in each packet. The sender performs hash calculation on packets and an authentication key. After packets carrying the calculation result arrive at the receiver, the receiver also performs hash calculation and compares the calculation result with the received calculation result. Any changes to the data during transmission will make the calculation result invalid. This implements data origin authentication and integrity verification. AH provides data integrity check on an entire IP packet.
ESP provides both authentication and encryption. An ESP header is appended to the standard IP header in each data packet, and the ESP Trailer and ESP Auth data fields are appended to each data packet. In contrast to AH, ESP encrypts the payload before encapsulating it into a data packet to ensure data confidentiality, and protects the IP header only in tunnel mode.
Key fields:
  Sequence Number: This field is a counter that monotonically increases from 1. It uniquely identifies a packet to prevent replay attacks.
  SPI: This field uniquely identifies an IPsec SA.
  Authentication Data: This field contains the Integrity Check Value (ICV) and is used by a receiver for data integrity check. Available authentication algorithms are MD5, SHA1, SHA2, and SM3.

## Slide 37: Encapsulation Modes
IPsec encapsulation is a process of adding AH or ESP fields to original IP packets for packet authentication and encryption. This process is implemented in transport or tunnel mode.
On the live network, the tunnel mode is often used for encapsulation.
Tunnel mode
Transport mode
IP Header | AH Header | Data
IP Header | ESP Header | Data | ESP Trailer | ESP Auth data
IP Header | AH Header | ESP Header | Data | ESP Trailer | ESP Auth data
AH
ESP
AH-ESP
New IP Header | AH Header | Raw IP Header | Data
New IP Header | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
New IP Header | AH Header | ESP Header | Raw IP Header | Data | ESP Trailer | ESP Auth data
AH
ESP
AH-ESP
Authenticated
Authenticated
Encrypted
ESP authenticated
Encrypted
AH authenticated
Authenticated
Authenticated
Encrypted
ESP authenticated
Encrypted
AH authenticated
IPsec Overview
IPsec Framework
Notes: In transport mode, an AH or ESP header is added between an IP header and a transport-layer protocol (TCP, UDP, or ICMP) header to protect the TCP, UDP, or ICMP payload. As no additional IP header is added, IP addresses in the original packets are visible in the IP header of the post-encrypted packet.
In tunnel mode, an AH or ESP header is added before the raw IP header and then encapsulated into a new IP packet with a new IP header to protect the IP header and payload.

## Slide 38
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
  Basic Concepts of IPsec
  IPsec Fundamentals
  IPsec Application Scenarios
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 39: IPsec Mechanism
IPsec mechanism
IPsec device
IPsec tunnel
IPsec device
IKE module
User data
User data
Encryption and authentication module
IKE SA negotiation
Exchange user data
IKE module
Encryption and authentication module
Encrypts, decrypts, and authenticates user data based on IPsec SA
IKE SA
IPsec SA
IPsec
SA negotiation
Encrypts IPsec SA negotiation packets based on IKE SA
IKE negotiation phase 1
IKE negotiation phase 2
IPsec SA
The device encrypts and decrypts protected flows
Notes: The IPsec mechanism is as follows:
  An IKE SA is negotiated in the first phase of IKE negotiation.
  The IKE SA is used to encrypt the packets in the second phase of IKE negotiation. That is, IPsec SAs are negotiated in the second phase of IKE negotiation.
  IPsec SAs are used to encrypt data.

## Slide 40: IKEv1
IKEv1 negotiation goes through two phases: In phase 1, two IPsec peers negotiate and establish a secure tunnel (an IKE SA). In phase 2, the two IPsec peers establish a pair of IPsec SAs for secure data transmission through the secure tunnel established in phase 1.
IKE module
IKE SA negotiation
IKE module
IKE SA
IPsec
SA negotiation
Encrypts IPsec SA negotiation packets based on IKE SA
IKE negotiation phase 1
IKE negotiation phase 2
IKEv1 negotiation process
IKEv1
IKEv2
Defining IPsec-Protected Data Flows

## Slide 41: IKEv1 Negotiation Phase (1)
In phase 1 of IKEv1 negotiation, an IKE SA is established. After an IKE SA is established, all the ISAKMP messages transmitted between two IPsec peers will be encrypted and authenticated. The secure tunnel established in phase 1 enables IPsec peers to communicate securely in phase 2.
Phase 1 of IKEv1 negotiation supports two negotiation modes: main mode and aggressive mode.
Main mode
Aggressive mode
Sends an IKE proposal
Searches for a matching IKE proposal
Accept the IKE proposal
Sends an acknowledged IKE proposal
Sends information for key generation
Generates keys
Generates keys
Sends information for key generation
Sends identity and authentication data
Verifies identity and exchanged data
Verifies identity and exchanged data
Sends identity and authentication data
Initiator
Responder
1
2
4
6
3
5
Sends IKE proposals, information for key generation, and identity information
Searches for matching algorithms, generates keys, and authenticates identity
Accepts the proposal and generates keys
Sends key generation information, identity information, and authentication data
Sends authentication data.
Verifies exchanged data.
Initiator
Responder
1
2
3
Encrypted data
IKEv1
IKEv2
Defining IPsec-Protected Data Flows
Notes: The main mode requires three exchanges between the peers, totaling six ISAKMP messages. The three exchanges are described as follows:
  Messages 1 and 2 are used for IKE proposal exchange.
    The initiator sends one or more IKE proposals to the responder. The responder searches for the first matching IKE proposal and then sends it to the initiator. IKE proposals of the initiator and responder match if they have the same encryption algorithm, authentication algorithm, authentication method, and DH group identifier.
  Messages 3 and 4 are used for key information exchange.
    The initiator and responder exchange the DH public value and nonce value to generate the IKE SA authentication key and encryption key.
  Messages 5 and 6 are used for identity and authentication information exchange. (Both parties use the generated keys to exchange information.)
    The initiator and responder use the generated keys to authenticate each other and the information exchanged in main mode.
The aggressive mode uses only three messages. Messages 1 and 2 are used to negotiate IKE proposals and exchange the DH public value, mandatory auxiliary information, and identity information. Message 2 also contains the identity information sent by the responder to the initiator for authentication. Message 3 is used by the responder to authenticate the initiator.
Compared with the main mode, the aggressive mode reduces the number of exchanged messages and speeds up the negotiation. However, the aggressive mode does not encrypt identity information.

## Slide 42: IKEv1 Negotiation Phase (2)
In IKEv1 phase 2, IPsec SAs need to be established and keys needs to be generated for securely transmitting data.
This phase uses the quick mode. This mode uses the keys generated in phase 1 to verify the integrity of ISAKMP messages and identities of the initiator and responder, and to encrypt ISAKMP messages, ensuring exchange security.
Quick mode
Sends IPsec proposals, identity, and authentication data
Searches for a matching IPsec proposal and generates keys
Accepts the proposal and generates keys
Sends the acknowledged IPsec proposal, identity, and authentication data
Sends acknowledged data
Accepts the information.
Initiator
Responder
1
2
3
Encrypted data
IKEv1
IKEv2
Defining IPsec-Protected Data Flows
Notes: In IKEv1 phase 2, two IPsec SAs are established through three ISAKMP messages:
  Message 1 is used by the initiator to send local security parameters and identity authentication information to the responder.
    Security parameters include protected data flows and parameters to be negotiated, such as an IPsec proposal. Identity authentication information includes the keys generated in phase 1 and keying materials generated in phase 2, and can be used to authenticate the peer again.
  Message 2 is used by the responder to send acknowledged security parameters and identity authentication information, and to generate new keys.
    The encryption key and authentication key used for secure data transmission over IPsec SAs are generated based on the keys generated in phase 1 and parameters such as the SPI and protocol. This ensures that each IPsec SA has unique encryption and authentication keys.
  Message 3 is used by the initiator to send acknowledged information to communicate with the responder. IKEv1 negotiation then ends and IPsec SAs are established.

## Slide 43: IKEv2
The process of establishing SAs through IKEv2 negotiation is much simpler than that through IKEv1 negotiation. In normal cases, IKEv2 can establish a pair of IPsec SAs through only four messages in two exchanges. One additional Create_Child_SA Exchange can be used to establish another pair of IPsec SAs if required, during which only two messages are exchanged.
IKEv2 defines three exchanges: Initial Exchanges, Create_Child_SA Exchange, and Informational Exchange.
IKEv1
IKEv2
Defining IPsec-Protected Data Flows

## Slide 44: IKEv2 Initial Exchanges
IKEv2 establishes the first pair of IPsec SAs through Initial Exchanges. Initial Exchanges involves four messages in two exchanges.
Initial Exchanges process
Initiator
Responder
Encrypted data
Sends IKE SA parameters
Searches for matching IKE SA parameters
Accepts the parameters
Sends the matching IKE SA parameters
Sends identity information
Verifies identity and exchanged data
Verifies identity and exchanged data
Sends identity information
2
4
1
3
IKEv1
IKEv2
Defining IPsec-Protected Data Flows
Notes: Messages 1 and 2 are used in exchange 1 (called IKE_SA_INIT). In exchange 1, IKE SA parameters are negotiated in plain text, including the encryption key, authentication key, random number, and DH key. After IKE_SA_INIT is complete, shared keying material is generated, from which all keys used by IPsec SAs are derived.
Messages 3 and 4 are used in exchange 2 (called IKE_AUTH). In exchange 2, identities of the two parties and the first two messages are authenticated, and IPsec SA parameters are negotiated. IKEv2 supports Rivest-Shamir-Adleman (RSA) signature authentication, pre-shared key (PSK) authentication, and Extensible Authentication Protocol (EAP) authentication. The initiator omits the AUTH payload in message 3 to indicate that EAP authentication is required.

## Slide 45: IKEv2 Create_Child_SA Exchange
After one pair of IPsec SAs is established based on an IKE SA, Create_Child_SA Exchange can be performed to negotiate more pairs of IPsec SAs. In addition, Create_Child_SA Exchange can be performed for IKE SA re-negotiation.
Create_Child_SA Exchange involves two messages in one exchange and corresponds to IKEv1 phase 2. The initiator in Create_Child_SA Exchange can be the initiator or responder in Initial Exchanges.
Create_Child_SA Exchange process
Initiator
Responder
Encrypted data
Sends identity information
Verifies identity and exchanged data
Verifies identity and exchanged data
Sends identity information
2
1
IKEv1
IKEv2
Defining IPsec-Protected Data Flows

## Slide 46: IKEv2 Informational Exchange
IKEv2 peers perform Informational Exchange to exchange control information, including error information and notifications.
Informational Exchange must be performed under the protection of an IKE SA. Specifically, Informational Exchange is performed after Initial Exchanges are complete. Control information may belong to an IKE SA or a child SA. Therefore, Informational Exchange must be protected by the IKE SA or the IKE SA based on which the child SA is established accordingly.
Informational Exchange process
Initiator
Responder
Encrypted data
Sends control information
Performs operations based on control information
Accepts the information
Responds to control information
2
1
IKEv1
IKEv2
Defining IPsec-Protected Data Flows

## Slide 47: Defining IPsec-Protected Data Flows
The data flows to be protected by IPsec can be defined using either of the following methods:
  Use ACLs.
    ACLs can be configured to define the data flows to be protected by an IPsec tunnel. The packets matching permit clauses in the ACLs will be protected.
  Use routes.
    Routes can be configured to define the data flows to be protected by an IPsec tunnel established through IPsec tunnel interfaces. All packets routed to these interfaces will then be protected.
On the live network, GRE over IPsec typically defines protected flows based on routes.
IKEv1
IKEv2
Defining IPsec-Protected Data Flows
Notes: The method of using routes has the following advantages:
  Simplifies the IPsec configuration: IPsec-protected data flows are routed to tunnel interfaces, without the need to use ACLs to define the characteristics of traffic to be encrypted or decrypted.
  Supports dynamic routing protocols.
  Protects multicast traffic through GRE over IPsec.

## Slide 48
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
  Basic Concepts of IPsec
  IPsec Fundamentals
  IPsec Application Scenarios
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 49: GRE over IPsec
Leveraging advantages of GRE and IPsec, GRE over IPsec encapsulates multicast, broadcast, and non-IP packets into ordinary IP packets and then securely transmits these IP packets through IPsec.
GRE over IPsec encapsulates packets using GRE and then IPsec.
GRE over IPsec data encapsulation (ESP)
Internet
IPsec tunnel
IPsec tunnel
GRE tunnel
IP data
IPsec data
IP data
Public IP
Data
GRE Header
Private IP
ESP Header
Public IP
Data
GRE Header
Private IP
ESP Header
Public IP
GRE over IPsec packet in transport mode
GRE over IPsec packet in tunnel mode
Notes: GRE over IPsec supports encapsulation in both tunnel and transport modes. An IPsec header needs to be added to packets if GRE over IPsec in tunnel mode is used, resulting in longer packets. In this case, packets are more likely to be fragmented. Therefore, GRE over IPsec in transport mode is recommended.
In the IP header added during IPsec encapsulation, the source and destination addresses are the IP addresses of the local interface and remote interface to which an IPsec policy is applied.
IPsec protects data flows from the GRE tunnel source to the GRE tunnel destination. In the IP header added during GRE encapsulation, the source and destination addresses are the source and destination addresses of a GRE tunnel.

## Slide 50: L2TP over IPsec
Layer 2 Tunneling Protocol (L2TP) over IPsec encapsulates packets using L2TP and then IPsec. It uses L2TP for user authentication and address allocation and uses IPsec for secure communication. L2TP over IPsec ensures that branches or traveling employees are securely connected to the headquarters.
L2TP over IPsec data encapsulation (ESP)
Internet
IPsec tunnel
IPsec tunnel
L2TP tunnel
PPP data
IPsec data
PPP data
L2TP over IPsec packet in transport mode
L2TP over IPsec packet in tunnel mode
Public IP
Data
PPP Header
Private IP
ESP Header
UDP Header
L2TP Header
Public IP
Data
PPP Header
Private IP
ESP Header
UDP Header
L2TP Header
Public IP
Notes: L2TP encapsulation and then IPsec encapsulation are performed on packets transmitted over an L2TP over IPsec tunnel. In the IP header added during IPsec encapsulation, the source and destination addresses are the IP addresses of the local interface and remote interface to which an IPsec policy is applied.
IPsec needs to protect the data flows from the L2TP tunnel source to the L2TP tunnel destination. In the IP header added to packets during L2TP encapsulation, the source and destination addresses are the source and destination addresses of an L2TP tunnel. When a branch connects to the headquarters, the source address of the L2TP tunnel is the IP address of the outbound interface on the L2TP access concentrator (LAC), and the destination address is the IP address of the inbound interface on the L2TP network server (LNS).
A public IP header is added to packets during L2TP encapsulation, and another public IP header is added to packets if L2TP over IPsec in tunnel mode is used, resulting in longer packets, which are prone to being fragmented. Therefore, L2TP over IPsec in transport mode is recommended.
The L2TP over IPsec negotiation process and packet encapsulation process are similar when traveling employees are remotely connected to the headquarters and when branch employees are connected to the headquarters. The difference is that, L2TP and IPsec encapsulation is performed on clients when traveling employees are remotely connected to the headquarters. The L2TP tunnel source address is the private address assigned to a client and can be any address in the IP address pool configured on the LNS. The L2TP tunnel destination address is the address of the inbound interface on the LNS.

## Slide 51
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
  NAT Fundamentals
  NAT Types
  NAT Traversal Technologies
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 52: Motivation Behind NAT
Private network
Network address translation (NAT) was proposed in 1994. NAT can be used when some hosts on a private network have been assigned local IP addresses (that is, dedicated IP addresses used only on the private network) and want to communicate with hosts on the Internet (without encryption).
NAT resolves the problem of insufficient public IP addresses and protects internal devices against external attacks.
NAT device
Internet
NAT for access from a private network to the Internet
SIP: private IP address
Data
SIP: public IP address
Data
NAT
DIP: private IP address
Data
DIP: public IP address
Data
NAT

## Slide 53: NAPT
Network address and port translation (NAPT) translates both IP addresses and port numbers for addresses in an address pool. In this way, 1:n mapping between public and private addresses is implemented, which effectively improves public address utilization.
Easy IP is a special type of NAPT. It maps all private network sessions to an egress address. That is, Easy IP can be understood as NAPT with one address in the NAT address pool.
NAT mapping table
Private network
Web server
200.1.2.3
122.1.2.1
NAT
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Internet
NAT address pool
122.1.2.2
122.1.2.3
SIP: 192.168.1.1
DIP: 200.1.2.3
Data
S Port: 10321
D Port: 80
Source address + source port translation
SIP: 122.1.2.2
DIP: 200.1.2.3
Data
S Port: 1025
D Port: 80
SIP: 200.1.2.3
DIP: 192.168.1.1
Data
S Port: 80
D Port: 10321
SIP: 200.1.2.3
DIP: 122.1.2.2
Data
S Port: 80
D Port: 1025
192.168.1.1/24
192.168.1.2/24
Destination address + destination port translation (return packets)
Notes: NAPT enables a public IP address to map multiple private IP addresses through ports. In this mode, both IP addresses and transport-layer ports are translated so that different private IP addresses with different source port numbers are mapped to the same public IP address with different source port numbers.
Due to a limited number of TCP/UDP ports (0–65535), an address can be mapped to a limited number of private network sessions. Based on the NAT address pool, NAPT can randomly map a private network session to an address in the address pool, reducing the number of private network sessions.
A NAT mapping entry is triggered by the first packet. When no traffic is transmitted for a period of time, the NAT mapping entry is automatically deleted to ensure security.
NAPT and Easy IP are also known as source NAT because they change only the source address and port number of a packet.

## Slide 54: NAT Server
NAT Server maps an internal server to a public network through a one-to-one mapping between a [public IP address:port number] and a [private IP address:port number]. This function is used when the internal server needs to provide services for the public network.
An external host proactively accesses the [public IP address:port number] to communicate with the internal server.
NAT mapping table
Private network
Private IP Address:Port | Public IP Address:Port
192.168.1.10:80 | 122.1.2.1:8080
200.1.2.3
Web server
192.168.1.10
122.1.2.1
NAT
Internet
SIP: 200.1.2.3
DIP: 192.168.1.10
Data
S Port: 1025
D Port: 80
SIP: 200.1.2.3
DIP: 122.1.2.1
Data
S Port: 1025
D Port: 8080
Destination address + destination port translation
SIP: 192.168.1.10
DIP: 200.1.2.3
Data
S Port: 80
D Port: 1025
Source address + source port translation
(return packets)
SIP: 122.1.2.1
DIP: 200.1.2.3
Data
S Port: 8080
D Port: 1025

## Slide 55: Route Advertisement in a NAT Address Pool
In some cases, the NAT device may not be the egress device, so the return traffic needs to be diverted to the NAT device. To achieve this, you can import user network routes (UNRs) to a routing protocol.
UNRs are generated by non-interface IP addresses and do not exist on any interface. In a NAT scenario, the device creates UNRs for addresses in the NAT address pool. For example, if the NAT address pool has addresses 122.1.2.2 and 122.1.2.3, the device automatically creates UNRs 122.1.2.2/32 and 122.1.2.3.3/32.
OSPF
Web server
Egress device
Internet
NAT address pool
122.1.2.2
122.1.2.3
IP routing table
122.1.2.2/32 UNR NH: Local
122.1.2.3/32 UNR NH: Local
NAT device
After an address pool is configured, 32-bit UNRs are automatically generated.
IP routing table
122.1.2.2/32 OSPF NH: R1
122.1.2.3/32 OSPF NH: R1
R1
Routes are transmitted through OSPF.

## Slide 56: Security Risks of the NAT Mapping Table
After forwarding a data packet, the NAT device generates a NAT mapping table. When receiving a return packet, the NAT device considers the packet valid and forwards it only when a matching NAT mapping entry is found.
If an external host uses the public IP address and port number in the NAT mapping table to send a packet, will the data be forwarded?
Private network
Web server
200.1.2.3
122.1.2.1
NAT
Internet
192.168.1.1/24
192.168.1.2/24
NAT address pool
122.1.2.2
122.1.2.3
PC1
PC2
External host
DIP: 122.1.2.2
Data
D Port: 1025
NAT mapping table
SIP: 192.168.1.1
DIP: 200.1.2.3
Data
S Port: 10321
D Port: 80
SIP: 122.1.2.2
DIP: 200.1.2.3
Data
S Port: 1025
D Port: 80
Source address +
source port number translation
SIP: 200.1.2.3
DIP: 192.168.1.1
Data
S Port: 80
D Port: 10321
SIP: 200.1.2.3
DIP: 122.1.2.2
Data
S Port: 80
D Port: 1025
Destination address + destination port number translation (return packets)
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Notes: There are four types of NAT:
  Full cone NAT
  Restricted cone NAT
  Port restricted cone NAT
  Symmetric NAT

## Slide 57
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
  NAT Fundamentals
  NAT Types
  NAT Traversal Technologies
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 58: Basic Concepts of NAT Types
NAT can be classified into two types: cone NAT and symmetric NAT.
Cone NAT is further classified into full cone NAT, restricted cone NAT, and port restricted cone NAT.
Concepts related to NAT types
  Internal tuple: a 2-tuple consisting of the private address and port number of an internal host, that is, the source address and source port number of a packet sent by the internal host.
  External tuple: a 2-tuple consisting of the public address and port number obtained after an internal tuple is translated using NAT, that is, the post-NAT source address and source port number of a packet received by an external host.
  Target tuple: a 2-tuple consisting of the address and port number of an external host, that is, the destination address and destination port number of a packet sent by an internal host.
SIP: 192.168.1.1
DIP: 200.1.2.3
Data
S Port: 10321
D Port: 80
Source address + source port number translation
SIP: 122.1.2.2
DIP: 200.1.2.3
Data
S Port: 1025
D Port: 80
Internal tuple
External tuple
Target tuple
Target tuple
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Internal tuple
External tuple
Target tuple
Notes: NAPT and Easy IP are also known as source NAT because they change only the source address and port number of a packet.

## Slide 59: Full Cone NAT
After PC1 on a private network communicates with the web server, the NAT device generates a NAT mapping table. If full cone NAT is used and an attacker sends a packet with the external tuple (122.1.2.2:1025) as the destination, the NAT device forwards this packet to PC1.
One internal tuple is translated into one external tuple by NAT. Any external host can send packets with the address and port number in the external tuple as the destination. When receiving such packets, the NAT device forwards them to the device corresponding to the mapping internal tuple. Full cone NAT is simple but has security risks.
Full cone NAT
Private network
Web server
200.1.2.3
122.1.2.1
NAT
Internet
192.168.1.1/24
192.168.1.2/24
NAT address pool
122.1.2.2
122.1.2.3
PC1
PC2
External host
202.2.2.1
DIP: 122.1.2.2
Data
D Port: 1025
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Internal tuple
External tuple
Target tuple

## Slide 60: Restricted Cone NAT
Restricted cone NAT is a restricted version of full cone NAT. When receiving a packet from an external host, the NAT device with restricted cone NAT enabled no only checks whether the destination address and port number of the packet are the same as those in the external tuple but also checks whether the source IP address of the packet is the same as the IP address in the target tuple. If both conditions are met, the packet is forwarded.
After PC1 on a private network communicates with the web server, the NAT device generates a NAT mapping table. If restricted cone NAT is used and an attacker sends a packet with the external tuple (122.1.2.2:1025) as the destination, the NAT device forwards this packet to PC1 only when the source address of this packet is the IP address (200.1.2.3) in the target tuple.
Restricted cone NAT
Private network
Web server
200.1.2.3
122.1.2.1
NAT
Internet
192.168.1.1/24
192.168.1.2/24
NAT address pool
122.1.2.2
122.1.2.3
PC1
PC2
External host
200.1.2.3
SIP: 200.1.2.3
DIP: 122.1.2.2
Data
S Port：2050
D Port: 1025
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Internal tuple
External Tuple
Target tuple

## Slide 61: Port Restricted Cone NAT
Port restricted cone NAT is a restricted version of restricted cone NAT. When receiving a packet from an external host, the NAT device with port restricted cone NAT enabled not only checks whether the source IP address and port number of the packet are the same as those in the external tuple but also checks whether the destination IP address and port number of the packet are the same as those in the target tuple. If both conditions are met, the packet is forwarded. This type of NAT is highly secure.
After PC1 on a private network communicates with the web server, the NAT device generates a NAT mapping table. If port restricted cone NAT is used and an attacker sends a packet with the external tuple (122.1.2.2:1025) as the destination, the NAT device forwards this packet to PC1 only when the source address and source port number of this packet are those in the target tuple (200.1.2.3:80).
Port restricted cone NAT
Private network
Web server
200.1.2.3
122.1.2.1
NAT
Internet
192.168.1.1/24
192.168.1.2/24
NAT address pool
122.1.2.2
122.1.2.3
PC1
PC2
External host
200.1.2.3
SIP: 200.1.2.3
DIP: 122.1.2.2
Data
S Port：80
D Port: 1025
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.3:80 | --------
Internal tuple
External tuple
Target tuple

## Slide 62: Symmetric NAT
When symmetric NAT is used, the same internal tuple and the same target tuple are translated into the same external tuple. However, if the internal or target tuple is different, they are translated into different external tuples. The NAT device with symmetric NAT enabled processes returned packets in a similar way to that with port restricted cone NAT enabled. Such a NAT device checks whether the source IP address + port number and the destination IP address + port number of a return packet are the same as those in the external tuple and target tuple, respectively.
When PC1 on a private network communicates with the web server and DNS server, the NAT device generates different NAT mapping entries for different targets, even if the source IP addresses and port numbers are the same. If symmetric NAT is used and an attacker sends a packet with the external tuple (122.1.2.2:1025) as the destination, the NAT device forwards this packet to PC1 only when the source address and source port number of this packet is the target tuple (200.1.2.3:53).
Symmetric NAT
Private network
Web server
200.1.2.2
122.1.2.1
NAT
Internet
192.168.1.1/24
192.168.1.2/24
NAT address pool
122.1.2.2
122.1.2.3
PC1
PC2
External host
200.1.2.3
SIP: 200.1.2.3
DIP: 122.1.2.3
Data
S Port: 53
D Port: 1025
NAT mapping table
Source | 192.168.1.1:10321 | 122.1.2.3:2231
Destination | 200.1.2.3:53 | --------
 | Private IP Address:Port | Public IP Address:Port
Source | 192.168.1.1:10321 | 122.1.2.2:1025
Destination | 200.1.2.2:80 | --------
DNS server
200.1.2.3
External tuple
Target tuple
Internal tuple

## Slide 63: NAT Application Scenarios
On the live network, NAPT or Easy IP generally uses symmetric NAT.
When NAT traversal is required on the live network, cone NAT can be used.
Application scenarios of NAT traversal
Internet
NAT device
NAT device
PC
PC
Full cone NAT
Full cone NAT

## Slide 64
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
  NAT Fundamentals
  NAT Types
  NAT Traversal Technologies
Intelligent Traffic Steering Technologies in WAN Interconnection

## Slide 65: Motivation Behind NAT Traversal
Private network
Although NAT enables users on a private network to access a public network, it has the following defects:
  NAT generates NAT mapping entries for the traffic from the private network to the public network. These entries have aging time. If a session between the two ends is silent for a long time, the connection is interrupted.
  The private IP addresses of users are translated into the same public IP address by NAT. However, because servers may restrict the access frequency of the same IP address to prevent DoS attacks, some users may fail to access the servers. Besides, some applications cannot effectively trace the original IP devices, making it difficult for network management and fault locating.
Multiple NAT traversal technologies are developed to solve the problems encountered by end-to-end IP applications in the NAT environment.
Private network
NAT traversal
Internet
NAT device
NAT device

## Slide 66: Existing NAT Traversal Technologies
Currently, the mainstream NAT traversal technologies are as follows:
  Universal Plug and Play (UPnP)
  Application Level Gateway (ALG)
  Middlebox Communications (MIDCOM)
  Full Proxy
  Session Traversal Utilities for NAT (STUN)
  Traversal Using Relay NAT (TURN)
  Interactive Connectivity Establishment (ICE)
  STUN and TCP too (STUNT)
This course describes ALG and STUN.

## Slide 67: Motivation Behind NAT ALG
Servers that provide various services (such as HTTP, DNS, and FTP) on the live network are usually deployed on a private network. Therefore, the NAT Server function needs to be deployed on the NAT device so that external users can access these services. However, some services use multi-channel protocols, such as FTP, DNS, and SIP. Deploying NAT Server cannot allow external users to access these services. For these multi-channel protocols, you can use NAT ALG to solve the problem.
NAT cannot enable external users to access the FTP server because FTP is a multi-channel protocol, regardless of whether active or passive FTP is used.
Challenges of multi-channel protocols to NAT (FTP)
Internet
NAT device
NAT device
DIP: IP3
Data
D Port: 21
IP1
IP2
IP3
IP4
DIP: IP3
Data
D Port: 21
DIP: IP4
Data
D Port: 21
The management channel is established, and the client is notified of the port used by the data channel.
DIP: IP3
Data
D Port: 1025
Passive FTP
DIP: IP3
Data
D Port: 1025
No related information exists in the NAT mapping table, and the data channel fails to be established.
Random target port allocated by the FTP server
The management channel is established and FTP control packets are exchanged.
The management channel is established and FTP control packets are exchanged.
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Destination | IP4:21 | IP3:21

## Slide 68: Fundamentals of NAT ALG
NAT ALG can parse the payload of packets, identify and translate important information (such as the destination port of the FTP data channel) in the payload, and generate NAT mapping entries based on the important information to enable external hosts to access the servers on a private network.
Challenges of multi-channel protocols to NAT (FTP)
Internet
NAT device
NAT device
DIP: IP3
Data
D Port: 21
IP1
IP2
IP3
IP4
DIP: IP3
Data
D Port: 21
DIP: IP4
Data
D Port: 21
The management channel is established and FTP control packets are exchanged.
DIP: IP3
Data
D Port: 1025
Passive FTP
DIP: IP3
Data
D Port: 1025
Random target port allocated by the FTP server
NAT ALG enabled
The management channel is established and FTP control packets are exchanged.
DIP: IP4
Data
D Port: 1025
Data channel established
Data channel established
IP header
FTP control packets
NAT mapping table
 | Private IP Address:Port | Public IP Address:Port
Destination | IP4:21 | IP3:21
Destination | IP4:1025 | IP3:1025
The management channel is established, and the client is notified of the port used by the data channel.
NAT ALG reads the FTP control packet, learns that the destination port of the FTP data channel is 1025, and generates a NAT mapping entry.

## Slide 69: Disadvantages of NAT ALG
NAT ALG needs to read protocol packets. For new protocols, the NAT ALG feature needs to be upgraded to support them. NAT ALG does not support proprietary multi-channel protocols.
A large number of devices on the live network do not support NAT ALG. As a result, the deployment cost is high.
NAT ALG solves the problems facing multi-channel protocols in the NAT Server scenario, but does not support the communication between hosts on private networks.

## Slide 70: Overview of STUN
In addition to NAT ALG, cone NAT can also be used for NAT traversal. It creates NAT mapping entries on NAT devices in advance and establish connections between private networks based on the NAT mapping entries.
STUN is mainly used to obtain the mapping between the private IP address + port and the post-NAT public IP address + port on the NAT device. The data channel for NAT traversal needs to be established in other modes.
NAT traversal
Private network
Private network
Internet
NAT device
NAT device
IP1
Port1
IP2
Port2
IP3
Port3
IP4
Port4
NAT mapping table
NAT mapping table
Private IP Address:Port | Public IP Address:Port
IP1:Port1 | IP2:Port2
Private IP Address:Port | Public IP Address:Port
IP4:Port4 | IP3:Port3
Notes: In RFC 3489, STUN is a complete NAT traversal solution and its full name is Simple Traversal of UDP Through NATs.
In the new RFC 5389 revision, STUN is positioned to provide a tool for NAT traversal rather than a complete solution. The full name of STUN is changed to Session Traversal Utilities for NAT. Besides the full name difference, STUN in RFC 5389 differs from STUN in RFC 3489 in that STUN in RFC 5389 supports NAT traversal for TCP.

## Slide 71: Fundamentals of STUN
STUN uses the client/server model. The STUN client and STUN server exchange packets to discover the NAT device and determine the IP address and port number allocated by the NAT device.
STUN fundamentals
Private network
Internet
NAT mapping table
IP1
Port1
Private IP Address:Port | Public IP Address:Port
IP1:Port1 | IP2:Port2
STUN server
STUN client
Address translation
SIP: IP1
STUN binding request
S Port: Port1
SIP: IP2
STUN binding request
S Port: Port2
Reads the source IP address and source port number of the data packet and adds them to the STUN binding response.
DIP: IP2
STUN binding response
D Port: Port2
Address translation
DIP: IP1
STUN binding response
D Port: Port1
The STUN client records the mapping between the private IP address + port number and the public IP address + port number.
IP=IP2, Port=Port2
NAT device
IP2
Port2
IP1:Port1 <-> IP2:Port2

## Slide 72: Application Example of STUN
Private IP Address:Port | Public IP Address:Port
IP4:Port4 | IP3:Port3
In an SD-WAN scenario, STUN can be used to interconnect post-NAT devices and establish data channels.
NAT traversal example
Private IP Address:Port | Public IP Address:Port
IP1:Port1 | IP2:Port2
Private network
Private network
Internet
IP1
Port1
IP2
Port2
IP3
Port3
IP4
Port4
STUN server
STUN client
STUN client
STUN binding request
STUN binding request
STUN binding response
STUN binding response
Learn the peer NAT information through BGP.
Send a STUN binding request.
Respond to the STUN binding request.
1
1
2
2
3
4
5
Establish a data channel for NAT traversal.
6
NAT device
NAT device
Notes: A STUN client sends a STUN binding request to the STUN server.
After receiving the STUN binding request, the STUN server obtains the source IP address and port number, constructs a STUN binding response, and sends the response to the client.
The STUN client obtains an IP address and port number from the binding response, and compares the obtained IP address and port number with the source IP address and port number carried in the binding request. If they are different, a NAT device is used in front of the STUN client.
STUN clients use BGP to learn each other's NAT information (IP addresses and port numbers before and after NAT).
The local STUN client uses the local pre-NAT IP address and port number and the pre-NAT IP address and port number of the peer STUN client to construct a STUN binding request and sends it to the peer STUN client. In addition, the local STUN client uses the local pre-NAT IP address and port number and the post-NAT IP address and port number of the peer STUN client to construct a STUN binding request and sends it to the peer STUN client. The peer STUN client performs the same operations.
After receiving the STUN binding request, the peer STUN client sends a STUN binding response to the local STUN client. The local STUN client performs the same operations.
After the preceding STUN messages are exchanged, a data channel is established between the STUN clients so that packets can traverse the NAT devices.

## Slide 73
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection
  SAC
  SRP

## Slide 74: Service Reliability
In the cloud computing era, network reliability cannot meet user requirements. Users want to understand the live network status based on applications and adjust the network based on the application status.
Such requirement poses the following challenges to traditional networks:
  Traditional networks cannot accurately identify applications.
  Traditional networks cannot be adjusted based on applications.
To cope with the challenges, two technologies are developed:
  Smart Application Control (SAC): This technology can flexibly identify applications.
  Smart Policy Routing (SPR): This technology can switch forwarding paths based on the network or application status.

## Slide 75: Overview of SAC
Traditional networks are managed based on traffic. However, in the cloud computing era, services are becoming increasingly important. Networks need to be managed and monitored based on applications instead of Five-tuple information.
Traditional routing and switching devices cannot identify application-layer information. Therefore, it is difficult to manage networks based on applications. Smart Application Control (SAC) technology helps routing and switching devices identify classified applications.
SAC uses service awareness (SA) and first packet identification (FPI) technologies to detect and identify Layer 4 to Layer 7 information (such as HTTP and RTP) in packets.

## Slide 76: SAC Signature Database
Signature identification is a basic function of SA technology. Different applications typically use different protocols, and different application protocols have their own signatures. A signature that can identify a protocol is known as a signature code. The system analyzes service flows passing through a device, and compares the analysis result with the signature database on the device. It identifies an application by detecting the signature code in data packets.
SAC signature databases include FPI and SA signature databases. FPI signatures refer to signatures for identifying FPI applications, and SA signatures refer to signatures for identifying SA applications.
SAC working mechanism
SAC detection
Signature database
Audio/Video optimization
QoS policy
Traffic policy
Service traffic
Signature matching
Matching voice and video
Matching a user-defined service
Matching the web page service
Notes: The SAC signature database file can only be updated through upgrades and cannot be manually modified.
The SAC signature database can be updated in either of the following modes:
  Online update: The SAC signature database can be updated through the security center platform or intranet update server.
  Local update: The upgrade package is downloaded from the security center platform and uploaded to the device through FTP for the update of the SAC signature database.

## Slide 77: SAC Application Identification Process
During SAC application identification, the system checks whether an application is identified. If the application is not identified, the system checks the FPI signature database and SA signature database in sequence.
Network device
FPI signature database
Service traffic
Signature matching
SA signature database
Signature matching
Application identification record
SAC detection
Traffic is directly forwarded at Layer 3 if the application has been identified.
Voice
Video
Web page
Download
Forwarding table
Notes: After a packet enters the device, the device determines whether the corresponding application has been identified based on the 5-tuple information carried in the packet. If the application has been identified, the device forwards the packet at Layer 3 without identifying the application again. If the application has not been identified, the device performs the SAC application identification process. The device then processes the packet based on the SAC identification result and forwards the packet at Layer 3. The SAC application identification process is as follows: The device identifies an application based on the ACL rules defined in FPI. If the application cannot be identified, the device identifies the application based on the DNS entries defined in FPI. If the application still cannot be identified, the device identifies the application based on the protocol and port mapping table defined in FPI. If the application still cannot be identified, the device starts the SA identification process.

## Slide 78: SA
After receiving data, the device can use service awareness (SA) technology to match applications.
SA uses the SA signature database to detect services. The existing SA signature database is embedded with more than 6000 applications, ensuring a high identification rate for public applications. In most cases, the SA signature database can only be updated online or locally and cannot be manually modified.
SAC detection
Service traffic
Signature matching
SA behavior signature matching
Voice
Video
Web page
Matching conditions | Application
Domain name, server IP address, and protocol | Voice
Domain name, server IP address, and protocol | Web page
Domain name, server IP address, and protocol | Video

## Slide 79: FPI
There is a problem in matching applications based on the SA signature code. That is, the application corresponding to the first several packets may fail to be identified based on the SA signature code. As a result, the processing on the first and subsequent packets may be inconsistent. First packet identification (FPI) enables a device to identify an application by matching the first packet of a flow.
FPI identifies applications based on 5-tuple information, DSCP values, protocols, and DNS domain names. The system provides a predefined FPI signature database to help SAC identify applications. You can also define FPI applications to identify new applications.
SAC detection
Service traffic
Signature matching
FPI signature database
Voice
Video
Web page
Matching conditions | Application
Destination IP1, EF | Voice
Destination Port1, protocol number 6 | Web page
Destination IP2, AF4 | Video
Notes: FPI applications are classified into the following types:
  Predefined and user-defined FPI applications based on the protocol and port number: These two types of applications are identified using entries that are generated based on the protocol and port number carried in packets. The difference is as follows: Packets of a predefined FPI application contain common protocols and port numbers, while packets of a user-defined FPI application contain the protocols and ports that you define.
  Predefined and user-defined FPI applications based on the DNS domain name: These two types of applications are identified using DNS entries generated through association between FPI and DNS. The difference is as follows: Packets of a predefined FPI application contain common DNS domain names, while packets of a user-defined FPI application contain the DNS domain names that you define.
  User-defined FPI application based on 5-tuple and DSCP information. This application is identified based on the user-defined 5-tuple and DSCP information using advanced ACL rules.
Identification process of FPI applications based on the DNS domain name
  FPI applications based on the DNS domain name are identified using DNS entries generated through association between FPI and DNS. The FPI signature database contains the mappings between domain names and applications. DNS response packets contain the mappings between domain names and IP addresses. Based on the mappings, a device generates DNS entries, which contain the mappings between IP addresses and applications. The device searches for DNS entries based on the IP address carried in the application protocol packets to identify the corresponding application.

## Slide 80
Common Networking Technologies in WAN Interconnection
Security Technologies in WAN Interconnection
NAT Traversal Technologies in WAN Interconnection
Intelligent Traffic Steering Technologies in WAN Interconnection
  SAC
  SRP

## Slide 81: Overview of SPR
In the cloud computing era, more users shift their attention from network connectivity to service availability, such as service response speed and service quality. However, traditional networks cannot detect link quality and service requirements, resulting in poor user experience.
Smart Policy Routing (SPR) addresses this problem. It actively detects the link quality and matches service requirements to select an optimal link to forward service data. SPR prevents network blackholes and flappings.
NQA
IP FPM
HQ
Branch
NQA
IP FPM
SRP deployment
SRP deployment

## Slide 82: SPR Service Differentiation
SPR differentiates traffic based on the protocol type, packet application, and packet information.
Different link quality parameter thresholds can be set for different services. You can set the delay (D), jitter (J), packet loss rate (L), and composite measure indicator (CMI).
CMI is calculated based on the delay, jitter, and packet loss rate.
SPR selects routes based on the CMI.
NQA
IP FPM
Branch
NQA
IP FPM
SPR module
TCP, UDP, GRE…
Source IP, Source Port, Destination IP…
DSCP, VPN, TCP-flag…
Based on the protocol type
Based on the packet application
Based on packet information
Notes: SPR classifies services based on the following attributes:
  Protocol types: IP, TCP, UDP, GRE, IGMP, IPINIP, OSPF, and ICMP
  Packet applications: DSCP, ToS, IP precedence, fragment, VPN, and TCP-flag
  Packet fields: Source IP Address, Destination IP Address, Protocol, Source Port, Destination Port, Source IP Prefix, Destination IP Prefix
When SPR selects routes for services based on the NQA detection result, the CMI is calculated using the following formula:
  CMI = 9000 – CMI-method. The default value of CMI-method is D + J + L.
  If NQA is used, a larger CMI value indicates better link quality.
When SPR selects routes for services based on the IP FPM detection result, the CMI is calculated using the following formula:
  CMI = D + J + L
  If IP FPM is used, a smaller CMI value indicates better link quality.

## Slide 83: SPR Detection Link and Link Group
SPR obtains quality indicators of detection links through probes (NQA or IP FPM) and then selects an optimal link.
A link group can contain one or more detection links.
SPR defines three roles for links: primary link group, backup link group, and best-effort link. When no suitable link is available in the primary and backup link groups, SPR activates the best-effort link to forward service data.
Network device
Internet
MPLS
LTE
Primary link group
Backup link group
Link detection
Link detection
Link detection

## Slide 84: SPR Link Selection
SPR periodically obtains the NQA or IP FPM detection result to determine whether a link meets service requirements. If the link does not meet service requirements, a link switchover is triggered.
The SPR link selection process is as follows:
Link selection based on the NQA test result
Link selection based on the IP FPM test result
The NQA detection result is read.
Is there a primary link whose quality meets service requirements?
Is there a backup link whose quality meets service requirements?
Is the CMI of the primary and backup link groups 0?
The best-effort link is started.
End
The link with the optimal CMI in the primary link group is used.
The link with the optimal CMI in the backup link group is used.
The link with the optimal CMI in the primary and backup link groups is used.
Yes
Yes
No
No
No
Yes
The IP FPM detection result is read.
Is there a primary link whose quality meets service requirements?
Is there a backup link whose quality meets service requirements?
Is the CMI of the primary and backup link groups 9000?
End
The link with the optimal CMI in the primary link group is used.
The link with the optimal CMI in the backup link group is used.
The link with the optimal CMI in the primary and backup link groups is used.
Yes
Yes
No
No
No
Yes
Notes: When a network is unstable, SPR triggers link switchovers frequently, which degrades service experience. SPR provides the flapping suppression function to address this problem.
The flapping suppression function is disabled by default, and the flapping suppression period is configurable. After traffic is switched to a new link, SPR starts the flapping suppression timer. Within a flapping suppression period, SPR does not perform a link switchover even if it does not obtain the NQA test result indicating that the link meets service requirements within a switchover period. After the flapping suppression timer expires, if SPR still does not obtain the NQA test result indicating that the link meets service requirements within a switchover period, SPR performs a link switchover. If SPR obtains the NQA test result indicating that the link meets service requirements within a switchover period, SPR retains traffic on the link without performing a link switchover.

## Slide 85: Using iMaster NCE to Implement SPR
During SPR deployment through iMaster NCE, to improve the site specifications on the entire network, separation between sites and application policies and traffic-triggered link selection are used together.
iMaster NCE maintains site adjacency information and application policies, and SPR is configured on routers. Traffic-triggered link selection allows for on-demand generation of SPR configurations. This prevents a large number of configurations from being created on the device and reduces the impact of link selection (based on IP FPM) on the CPU, significantly reducing the burden on the device.
iMaster NCE can use SAC to classify service traffic based on applications.
Site adjacency list
Application policy table
Site policy table
Triggering IP FPM link selection
IP FPM link selection
Generated dynamically
Site adjacency list
Application policy table
iMaster NCE
Network device

## Slide 86
(Multiple-answer question) Which of the following are private line technologies? ( )
  SDH
  L2TP
  MPLS VPN
  IPsec VPN
(True or false) SRP technology can flexibly select egress links based on the link quality. ( )
  True
  False
Notes: AC
A

## Slide 87
GRE over IPsec is used for WAN interconnection, and L2TP over IPsec is used for remote intranet access.
Based on IKE SA information, IPsec SA information can be securely transmitted on the public network. Based on IPsec SA information, service data can be securely transmitted on the public network.
To establish a WAN connection between two private network devices, you need to use a NAT traversal technology. The common NAT traversal technology is STUN.
To ensure WAN reliability, the link quality needs to be detected first, and then a proper egress or egress link is selected based on the link quality through specific technologies.