## Slide 1
Datacom
General
V1.0
He Junjian/WX580230
2021.06.03
Zhu Shigeng/00261992
New
Wu Yue/WX291773
2021.9.29
Yu Sheng/WX1092303
Update

## Slide 2: Enterprise Bearer WAN Solution

## Slide 3
A wide area network (WAN) is a computer network that connects local area networks (LANs) or metropolitan area networks (MANs) in different regions. A WAN allows information and network resources to be shared in a large scope.
An enterprise IP bearer WAN is a backbone WAN used to implement cross-region communication inside an enterprise. In enterprise network scenarios, various sectors, such as government, finance, education, and power, widely use IP bearer WANs to connect sites and clouds in different geographical locations, facilitating digitalization.
This course first describes basic WAN concepts and the evolution of WAN bearer technologies, and then introduces Huawei's CloudWAN solution and key technologies.

## Slide 4
On completion of this course, you will be able to:
  Describe the basic concepts of the WAN.
  Describe the trend, challenges, and evolution of the IP bearer WAN.
  Describe Huawei's CloudWAN solution.
  Describe the key technologies of Huawei's CloudWAN solution.
  Describe the typical industry application scenarios of Huawei's CloudWAN solution.

## Slide 5
Enterprise IP Bearer WAN Overview
CloudWAN Solution Overview
Typical Application Scenarios of the CloudWAN Solution

## Slide 6: Enterprise WAN Overview
Enterprise WAN definition
The enterprise WAN is used to implement cross-region communication inside an enterprise.
The enterprise WAN provides interconnection between the enterprise HQ and branches, between the enterprise and clouds, and between clouds.
Classification by purpose
Self-built, for internal use
Self-built, for external use
Enterprise HQ
Enterprise WAN
Enterprise
Cloud
Enterprise branch
Public cloud
Industry cloud
Private cloud
Data center

## Slide 7: Enterprise IP bearer WAN
Enterprise HQ
Enterprise IP bearer WAN
Network egress
Network egress
Enterprise branch
Public cloud
Industry cloud
Private cloud
Data center
Built by the enterprise or carrier
Enterprise WAN = Enterprise network egress + enterprise IP bearer WAN (built by the enterprise or carrier)

## Slide 8: Three Types of WAN Connections Provided by Carriers
Carriers provide three types of WAN connections for enterprises: Internet, MPLS private lines, and transmission private lines.
Internet
Provides Internet access services for common users and enterprises.
MPLS private line
Provides MPLS L3VPN and L2VPN services for large enterprises.
Transmission private line
Provides transmission private lines, such as SDH, MSTP, bare fiber, and WDM/OTN private lines, for large enterprises. Enterprises build their own IP bearer networks over transmission private lines.
Individual user
Enterprise campus
Data center
Internet
MPLS network
L3VPN
L2VPN
Transmission private line
Enterprise's self-built backbone network
Dial-up line
xDSL, xPON
BGP
Notes: Internet:
  Site-to-Internet private line: Ethernet private line/xPON private line/xDSL private line. The access is restricted by geographic locations. It applies to inter-enterprise communication over Internet-based encrypted tunnels.
  Dial-up connection: low bandwidth and low tariff. The access is not restricted by geographical locations. It applies to individual users.
  BGP: applies to data center Internet egresses.
As technologies are constantly developing, historical WAN technologies such as T1/E1, PSTN, ATM, and frame relay are not described here.

## Slide 9: Typical Logical Architecture of the Enterprise IP Bearer WAN
The typical architecture of the enterprise bearer WAN is divided into three layers: access layer, aggregation layer, and core layer.
Aggregation layer
Core layer
Access layer
Access layer (CE-PE):
Provides access for data centers in different cities.
Provides access for branches in different cities.
Provides access for external services in different cities.
Aggregation layer (PE-P):
Aggregates and transmits different types of services to the core layer based on physical locations.
Core layer (P):
Generally adopts the Full-mesh + dual-plane architecture.
It forwards traffic between different regions over stable, reliable, and service quality-guaranteed connections.

## Slide 10: Typical Bearer Technologies of the Enterprise IP Bearer WAN
Transmission line
IP bearer
All services are carried over the same IP network, and IP addresses are used to differentiate services.
This bearer mode applies to small- and medium-sized enterprises or networks that do not have specific service isolation, differentiated SLA, or traffic engineering requirements.
IP traffic forwarding
IGPs such as OSPF
Transmission line
MPLS bearer
Data is encapsulated into MPLS packets and forwarded based on labels.
VPNs are used to differentiate services. Service isolation and SLA assurance are supported.
The WAN VPN architecture consists of the data plane and control plane. The data plane uses MPLS, and the control plane uses MP-BGP. This bearer mode applies to large enterprises.
MPLS domain
MP-BGP
PE
PE

## Slide 11: Enterprise IP Bearer WAN Moving Towards the IPv6+ Era
Best effort, manual O&M
Static policy, semi-automatic O&M
IPv6 + protocol innovation + AI
5G & cloud era
Intelligent IP
Connectivity of everything, flexible connections, intelligent O&M
IPv4
MPLS
IPE
Internet IP
All IP

## Slide 12: Enterprise IP Bearer WAN Technologies Evolving Towards SRv6
With the development of technologies and service requirements, VPN becomes the mainstream bearer technology adopted by the WAN. The control and forwarding plane technologies of the WAN keep evolving.
The bearer WAN continuously evolves towards segment routing (SR) and IPv6.
MPLS
SR-MPLS
SRv6
Forwarding plane
Control plane
LDP
RSVP-TE
IGP
Simplifying the control plane
IGP + SR extension
IGP + SR extension
BGP (L3 service)
BGP for service
BGP for service
Payload
IPv6 header + SRH
BGP-LU (inter-AS)
Payload
VXLAN/GRE/L2TP, etc.
MPLS labels
Payload
VXLAN/GRE/L2TP, etc.
MPLS labels
Continuing control plane simplification
Evolvable
Notes: BGP Labeled Unicast (BGP-LU) (RFC 3017) is both an inter-AS and an intra-AS routing protocol.

## Slide 13
Enterprise IP Bearer WAN Overview
CloudWAN Solution Overview
Typical Application Scenarios of the CloudWAN Solution

## Slide 14: Two Major Changes Brought by Digital Transformation
1. Cloudification of millions of enterprises
2. IP-based production network
Public cloud
Power cloud
Financial cloud
Government cloud
Financial cloud
Finance
Government
Power
Transportation
Cloud adoption by enterprises
Local processing > Service cloudification
Multi-cloud adoption by enterprises
Private cloud > Hybrid cloud
Multiple TDM private networks > One IP bearer network
IEC and UIC propose IP-based transformation for power and transportation sectors, respectively.
Power relay protection
Train control and dispatching
Fuel pipe safety detection
Traditional relay protection > Wide-area relay protection
Manual monitoring > Over-the-horizon monitoring
Manual inspection > UAV inspection
Any access, flexible connection
Delay < 5 ms
Bandwidth > 100 Mbit/s
Multicast technology
Clock precision < 3 µs

## Slide 15: 3 Challenges Facing the WAN in the Cloud Era
Cloudification of millions of enterprises
How can networks be as agile as clouds?
Production service bearer
Can IP provide deterministic experience?
Connection scale x 100 ↑
How can O&M be simpler and networks more reliable?
Public cloud
DC1
DC2
Branch
Branch
Branch
Service deployment time
Dozens of days
< 1 hour
Relay protection
10 ms
One-way delay
200 µs
Two-way delay variation
A failure to meet these requirements may mean a protection failure, incurring accidents.
Train control
10 ms
One-way delay
50 ms
Failover duration
A failure to meet these requirements may mean train out-of-control.
Connection x 100
0 artifact, 0 frame freezing
24/7 online

## Slide 16: CloudWAN 3.0: Leading WANs into the Intelligent Cloud-Network Era
SRv6
FlexE-based slicing
One-fiber multipurpose transport: deterministic experience
Hierarchical slicing
Patented fingerprint-based slicing technology, simplifying deployment
One-network wide connection: network digitalization
Hop-by-hop detection technology, real-time visualization of network-wide status, troubleshooting within minutes
One-hop cloud access: flexible cloud-network connection
SRv6 enables service provisioning within minutes and agile service cloudification.
One-click fast scheduling: cloud-network coordinated scheduling
SDN + intelligent cloud-map algorithm, improving cloud-network resource utilization
Manager
Controller
Analyzer
IFIT
NETCONF/YANG
Township/outlet
Prefecture/Tier-1 branch
Province/ Ministry/HQ
County/Tier-2 branch
DC
Integrated security, all-round security protection
Qiankun security cloud service, proactively identifying cyber security threats
IPv6+ lays the foundation for the digital infrastructure.

## Slide 17: CloudWAN 3.0: Management, Control, and Analysis Platform + Intelligent Universal Service Routers for the Cloud Era
Network management
Metro router
NetEngine 40E universal service router
NetEngine 9000
Backbone router
NetEngine 9000-20
NetEngine40E-X16A
iMaster NCE = U2000 (management) + Controller (control) + uTraffic (analysis)
NetEngine40E-X8A
NetEngine 8000 Smart router
NetEngine 8000
M8
NetEngine 8000
M6
NetEngine 8000
F1A
NetEngine 8000
M1A/M1C

## Slide 18: CloudWAN 3.0: Management, Control, and Analysis Platform iMaster NCE-IP
Analysis
Controller
Management
NE management: topology, alarm, configuration, and inventory management
Service management: tunnel and VPN service management
Centralized path computation: path computation based on multiple constraints
Logical topologies: cost, delay, and bandwidth topologies
Network optimization: service path adjustment and optimization
Basic network analysis: display and analysis of performance, traffic, and quality
Analysis-based prediction: traffic, fault, and exception prediction
E2E SRv6
Backbone
Metro
Metro
NETCONF/YANG
Telemetry
Simplified architecture, intelligent connection, intelligent O&M
Manager
Controller
Analyzer

## Slide 19: One-Hop Cloud Access: SRv6-based Fast, Simplified Service Provisioning Across Domains
Siloed networks, isolated data islands
Layered and segmented networks, difficult for cloud access
Multi-cloud data convergence and sharing
SRv6-based one-hop cloud access, enabling fast provisioning
Cloudification of numerous industries
Education
Healthcare
Government
Education data
Healthcare data
Government data
Education private network
MPLS
MPLS
MPLS
Healthcare private network
MPLS
MPLS
MPLS
Government private network
MPLS
MPLS
MPLS
AS
AS
AS
AS
AS
AS
AS
AS
AS
Education, healthcare, government...
Education
Healthcare
Government
AS
AS
AS
AS
AS
AS
AS
AS
AS
SRv6
SRv6
SRv6
Protocol simplification: replacement of multiple original network protocols with SRv6 + IGP/BGP
E2E connection: E2E service provisioning across domains, overcoming the limits of MPLS-based segment-by-segment service provisioning
Automatic provisioning: Controller + SRv6, enabling automatic service provisioning within minutes
Notes: In the past, most of our networks were siloed private networks, such as education, healthcare, and government private networks. These networks were independent physical private networks and could not communicate with each other. The handling of some services may involve multiple private networks. Moreover, a service may be deployed segment by segment even on one private network. For example, multiple ASs may exist on a network due to the division of administrative domains, and one network service may be deployed across ASs (on a common network, service data is generally carried over MPLS). In this situation, a large number of device configurations and personnel communication are required. The network administrator needs to perform a large number of configurations on AS boundary devices, and it takes a long time to migrate the service to the cloud. The acceleration of enterprise digital transformation drives alignment between networks and clouds.
Now, increasingly more industries are deploying data to the cloud, making it easier to converge or share data. The introduction of SRv6 can remove process barriers and accelerate service provisioning. Simply put, SRv6 can be deployed on both ends of an SRv6 tunnel to implement one-hop cloud access.
In the MPLS era, a large number of control-plane protocols, such as IGP, BGP, LDP, and RSVP-TE, are required to carry VPN services on a network or implement traffic engineering. On the forwarding plane, there are protocols such as MPLS, GRE, and L2TP or native IP. The network configuration and configuration modification are complex. Huawei's CloudWAN solution simplifies network deployment by replacing multiple network protocols with SRv6+IGP/BGP. SRv6 uses IPv6 as the forwarding plane protocol. On a WAN where IPv6 is deployed, it is easy to deploy an end-to-end tunnel, even in inter-AS scenarios. The SDN controller can be used to implement automated SRv6 service provisioning within minutes.

## Slide 20: One Fiber Multipurpose Transport: Hierarchical Slicing for Refined, Deterministic Experience Assurance
Remote control
Video surveillance
Enterprise office
Production private network
Office private network
Media cloud
Collaboration cloud
Remote control
Video surveillance
Enterprise office
10+ private networks > 1 network with N slices
Good balance
Multi-network convergence
Private network experience
Hierarchical slicing: implements flexible bearer of multiple services and reduces network construction costs.
Differentiated network services: provide differentiated SLAs for diversified service requirements.
Slice lifecycle management: uses the controller for slice planning, construction, maintenance, and optimization.
Slice 1
Slice 2
Slice 3
One private network
Security protection video cloud
Notes: Huawei uses the hierarchical slicing technology to power IP-based production networks, ensuring deterministic SLAs for production services.
In the past, production and office services were carried over multiple independent private networks. Repeated network construction resulted in high investment costs and complex O&M of multiple networks. By deploying multiple slices on one IP bearer network, production services such as remote industrial control and video surveillance are directly isolated from office services, delivering 100% bandwidth guarantee for mission-critical services.

## Slide 21: One-Network Wide Connection: Providing a Service-Level SLA Measurement Solution with Higher Precision
Hop-by-hop delay
Packet loss location
Path restoration
1
2
3
Coloring: service identification
Counting and timestamping
Analysis
Telemetry
Telemetry
Telemetry
 | Delay (ms) | Jitter (ms) | Packet loss rate
Service 1 | 500 | 300 | 0.0001%
Service 2 | 100 | 30 | 0
Service 3 | 10 | 10 | 0
E2E/hop-by-hop KPI measurement
KPIs: delay, packet loss, jitter
Service mode: MPLS/SR/SRv6/L3VPN/EVPN
10-6 high precision and real services
Measurement based on real service flows
High precision: packet loss measurement precision as high as 10-6
Easy deployment
On-demand hop-by-hop measurement (for purposes such as detection of E2E KPI threshold-crossing events)
Complete configurations are required only on the ingress and egress.
Notes: iFIT integrates the RFC 8321 coloring technology and in-band detection technology to directly measure service packets. It works with second-level telemetry data collection and iMaster NCE for unified management, computation, and visualization. In this way, it implements real-time visualization and proactive monitoring of network quality SLAs and fast fault demarcation and locating.

## Slide 22: One-Click Fast Scheduling: Cloud-Network Coordinated Scheduling, Improving Cloud-Network Resource Utilization
Unbalanced cloud-network loads, wasting investments
Cloud-network coordinated optimization for efficient utilization of cloud-network resources
DC1
DC2
DC3
Intelligent cloud-map algorithm
Cloud management platform
Cloud resource information
90%
12%
25%
DC1
DC2
DC3
45%
50%
47%
Computing power
Cost
Storage
Cloud factors
Network factors
Bandwidth
Reliability
Delay
The intelligent cloud-map algorithm combines the cloud and network factors.
Load balancing is performed based on service conditions and cloud loads. Services are intelligently scheduled to the most appropriate cloud based on SRv6 and SDN technologies.
1
Traffic optimization based on network factors
2
Cloud access based on cloud factors
Before
Now

## Slide 23
Enterprise IP Bearer WAN Overview
CloudWAN Solution Overview
Typical Application Scenarios of the CloudWAN Solution

## Slide 24: e-Government Extranet of a Certain Province
Average daily visits to cloud services: 40,000+
Service cloudification time
Weeks
Hours
89.9%
System cloudification rate
Before
Now
Cloud-network separation: difficult for the network to match cloud agility
Cloud-network integration: multi-cloud access through one network
HRSS
Civil affairs
Healthcare
Provincial government
Municipal government
Policing
Municipal government
Provincial government
Policing
HRSS
Civil affairs
Healthcare
Surveillance
Surveillance
Silos: uncoordinated cloud-network resource scheduling
Slow provisioning: cross-domain configuration and service provisioning within weeks
Poor experience: network congestion upon traffic bursts
Coordination: cloud-network synergy and coordinated cloud-network services
Fast provisioning: automatic cross-domain provisioning within hours
Optimal experience: optimized services for user experience assurance
SDN + SRv6
Integrated digital government platform
Notes: Quick Network Adjustment upon Cloud Changes, Integrated Service Provisioning, Cloud-based Data Sharing.

## Slide 25: Intelligent Traffic Optimization on an Enterprise WAN
Service scenarios
Solution
The average traffic between the HQ and branches increases by about 20% annually, but the annual private line leasing budget is only allowed to increase by 5%.
The average private line utilization is only about 25%.
Enterprise data synchronization services run at night and require ultra-large bandwidth. On traditional networks, traffic load balancing is difficult to implement due to the shortest path first principle.
Before
Now
Utilization: 60%
Utilization: 5%
DC1
Beijing
DC2
Beijing
DC
Shanghai
Branch 1
Branch 2
Branch 3
Policy-based routing is manually configured hop by hop. A single optimization operation takes more than 2 hours and is prone to errors.
Traffic optimization often needs to be performed at night and requires the attendance of dedicated personnel.
DC1
Beijing
DC2
Beijing
DC
Shanghai
Branch 1
Branch 2
Branch 3
Per-hop configuration
IP policy-based routing
Automatic SRv6 Policy configuration
"We hope that traffic optimization can be automatically or manually triggered based on factors such as time range, traffic threshold, and traffic burst."
— Senior network architect

## Slide 26: Multi-Service Bearer Through Network
Relay protection
Production and O&M
Video surveillance
Dispatch phone
WAMS
Office phone
Campus surveillance
DCN
Office automation
Customer service
Various office services
Dispatch phone
Video surveillance
Production and O&M
Relay protection
FlexE slice 1
FlexE slice 2
FlexE slice 3
FlexE slice 4
Flexible, convenient service deployment
Support for network evolution over the next 10 years:
Smooth upgrade to 100/200 Gbit/s
Smooth evolution to SRv6/SR/EVPN
Unified bearer: NCE is used to deploy network resources in a unified manner for power service transport, achieving intelligent optimization.
Physical network slicing: TDM-based FlexE divides a physical network into multiple slices on demand to isolate different services and ensure service SLAs.
Office service
Production service

## Slide 27
(Single-answer question) In Huawei's CloudWAN solution, which of the following technologies can absolutely ensure the bandwidth of key services?( )
  SRv6 Policy
  FlexE-based network slicing
  iFIT
  Telemetry
Notes: B

## Slide 28
An enterprise IP bearer WAN is a backbone WAN used to implement cross-region communication inside an enterprise. In enterprise network scenarios, various sectors, such as government, finance, education, and power, widely use IP bearer WANs to connect sites and clouds in different geographical locations, facilitating digitalization.
Bearer WAN technologies evolve from MPLS to SRv6. In the cloud era, networks are expected to meet requirements regarding visualization, awareness, optimization, deterministic delay, openness, and programmability.
Huawei's CloudWAN solution meets all the preceding requirements. We will explore more about this solution in subsequent learning.