## Slide 1
Datacom
General
V1.0
He Junjian/WX580230
2021.2.22
Liu Shuying/00245623 & Wang Qiusheng/00287740
New
He Junjian/WX580230
2021.4.12
Wan Changli/WX408647
Update
Wu Yue/WX291773
2021.9.28
Lu Yueyue/WX445705
Update

## Slide 2: Segment Routing

## Slide 3
Segment Routing (SR) is designed to forward data packets on a network using the source routing model.
This document describes the source routing model of SR, segment definition, differences between SR-MPLS and SRv6, and scenario-specific SR-MPLS applications for Huawei NetEngine series routers.

## Slide 4
On completion of this course, you will be able to:
  Describe the background of SR.
  Describe the technical advantages of SR.
  Describe the basic concepts involved in SR.
  Describe the forwarding fundamentals of SR.
  Master basic SR-MPLS configurations.

## Slide 5
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing

## Slide 6: Problems in MPLS LDP and RSVP-TE
MPLS LDP
RSVP-TE
R1
R2
R4
R3
IGP
LDP itself does not have the path computation capability and requires an IGP for path computation.
Both the IGP and LDP need to be deployed for the control plane, and devices need to exchange a large number of packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
If LDP-IGP synchronization is not achieved, data forwarding may fail.
RSVP-TE configuration is complex and load balancing is not supported.
To implement TE, devices need to exchange a large number of RSVP packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
RSVP-TE uses a distributed architecture, so that each device only knows its own state and needs to exchange signaling packets with other devices.
LDP
LDP
LDP
LDP
IGP
IGP
IGP
R1
R2
R4
R3
RSVP response
RSVP response
RSVP request
RSVP request
Notes: In essence, MPLS is a tunneling technology used to guide data forwarding and has complete tunnel creation, management, and maintenance mechanisms. For the preceding mechanisms, networks are driven by network operation and management requirements, not by applications.

## Slide 7: Service-Driven Network: Services Define the Network Architecture
The development of 5G and cloud services has changed the attributes and scope of network connections. More requirements are raised on connections, such as requiring better SLA guarantee, deterministic latency, or more information to be carried in packets.
In this situation, the model that requires networks to adapt to services cannot keep up with rapid service development and even complicates network deployment and maintenance.
To address this issue, the service-driven network model can be used, so that the network architecture is defined by services. Specifically, after an application raises requirements (e.g. latency, bandwidth, and packet loss rate), a controller is used to collect information (e.g. network topology, bandwidth usage, and latency) and compute an explicit path according to the requirements.
Download service
Video service
Voice service
High bandwidth
Low latency
Low packet loss rate
Service-driven network
Notes: Traditionally, IP data packet forwarding is implemented based on IP addresses reachable to the destination over the shortest path. To meet the reliability requirements of services such as voice, online gaming, and video conferencing, the FRR technology is introduced. To meet the high bandwidth requirements of private line services such as group customer services, the TE technology is introduced. These technologies all represent network adaptation to services.
The increasing types of services pose a variety of network requirements. For example, real-time Unified Communications and Collaboration (UC&C) applications usually prefer to paths with low latency and jitter, and big data applications prefer to high-bandwidth tunnels with a low packet loss rate. In this situation, the model that requires networks to adapt to services cannot keep up with rapid service development and even complicates network deployment and maintenance.
The solution to this issue is to enable services to drive networks and define the network architecture. Specifically, after an application raises requirements (e.g. latency, bandwidth, and packet loss rate), a controller is used to collect information (e.g. network topology, bandwidth usage, and latency) and compute an explicit path according to the requirements.

## Slide 8: SR Roadmap
Service-defined network
Simplifies protocols and extends existing protocols.
  The extended IGP/BGP supports label distribution. Therefore, LDP is not required on the network, achieving protocol simplification. In addition, devices require only software upgrades instead of hardware replacement, protecting the investment on the live network.
  The source routing mechanism is introduced.
  The specific forwarding policy is instantiated as a label list on the ingress to control the traffic forwarding path.
Enables networks to be defined by services.
  After an application raises requirements (e.g. latency, bandwidth, and packet loss rate), a controller is used to collect information (e.g. network topology, bandwidth usage, and latency) and compute an explicit path according to the requirements.
R2
R4
R3
Controller
R1
IGP/BGP

## Slide 9: SR Solution
After services raise network requirements (e.g. latency, bandwidth, and packet loss rate), a controller computes an explicit path in a centralized manner and delivers an SR path to carry the services.
High bandwidth
Low latency
Low packet loss rate
PCEP/NETCONF/BGP
High-bandwidth path
Low-latency path
Low-packet-loss-rate path
Controller
Service requirement
Explicit path
Data download
Video
Voice

## Slide 10: SR Overview
SR is designed to forward data packets on a network using the source routing model.
SR divides a network path into several segments and assigns a segment ID (SID) to each segment and forwarding node. The segments and nodes are sequentially arranged into segment lists to form a forwarding path.
SR encapsulates segment list information that identifies a forwarding path into the packet header for transmission. After a node receives the packet, it parses the segment list information. If the top SID in the segment list identifies the local node, the node removes the SID and executes the follow-up procedure. Otherwise, the node forwards the packet to the next hop in equal cost multiple path (ECMP) mode.
SR has the following characteristics:
  Extends existing protocols (e.g. IGP) to facilitate network evolution.
  Supports both controller-based centralized control and forwarder-based distributed control, providing a balance between the two control modes.
  Enables networks to quickly interact with upper-layer applications through the source routing technology.
Notes: https://datatracker.ietf.org/doc/rfc8402/

## Slide 11: SR Advantages
Simplified control plane of the MPLS network
SR uses a controller or IGP to uniformly compute paths and allocate labels, without the need to use tunneling protocols such as RSVP-TE and LDP.
SR can be directly used in the MPLS architecture, without requiring changes to the forwarding plane.
Efficient TI-LFA FRR protection against path failures
SR works with remote loop-free alternate (RLFA) FRR to provide efficient topology-independent loop-free alternate (TI-LFA) FRR.
TI-LFA FRR offers node and link protection for all topologies, addressing the weakness in traditional tunnel protection technologies.
Enhanced network capacity expansion capability
MPLS TE is a connection-oriented technology. To maintain connection states, devices need to exchange and process numerous keepalive packets, straining the control plane.
SR can control any service path by merely performing label operations for packets on the ingress. It does not require transit nodes to maintain path information, thereby freeing up the control plane. Moreover, the SR label quantity is the sum of the node quantity and local adjacency quantity on the entire network, meaning that it is related only to the network scale, rather than the tunnel quantity or service volume.
Smoother evolution to SDN networks
As SR is designed based on the source routing model, the ingress controls packet forwarding paths.
SR can work with the centralized path computation module to flexibly and easily control and adjust paths.
SR supports both traditional networks and SDN networks and is compatible with existing devices, ensuring smooth evolution to SDN networks.

## Slide 12
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing

## Slide 13: Basic Concept: Segment
A segment represents an instruction to be executed by a node for a received data packet, and the instruction is encapsulated in the packet header.
For example:
  Instruction 1: Forward the packet to R4 over the shortest path (ECMP supported).
  Instruction 2: Forward the packet through GE0/0/2 of R4.
  Instruction 3: Forward the packet to R8 over the shortest path.
1
1
2
3
R4
R6
R8
R1
R2
R3
R5
R7
GE0/0/2
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 14: Basic Concept: Segment ID
Segment IDs (SIDs) identify segments. The SID format depends on the specific technical implementation. For example, SIDs can be MPLS labels, indexes in an MPLS label space, or IPv6 addresses.
A segment list is an ordered list of one or more SIDs.
For example:
  Instruction 1 (400): Forward the packet to R4 over the shortest path (ECMP supported).
  Instruction 2 (1046): Forward the packet through GE0/0/2 of R4.
  Instruction 3 (800): Forward the packet to R8 over the shortest path (ECMP supported).
1
1
2
400
1046
800
3
R4
R6
R8
R1
R2
R3
R5
R7
GE0/0/2
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: The label values used in this course are only examples. For details about the label allocation scope, see the corresponding product documentation.

## Slide 15: Basic Concept: Source Routing
1
1
2
400
1046
800
3
R4
R6
R8
R1
R2
R3
R5
R7
GE0/0/2
400
1046
800
Source routing: The source node selects a forwarding path and encapsulates an ordered segment list into a packet. After receiving the packet, other nodes forward it based on the segment list information.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 16: Basic Concept: Segment Classification
1001
1002
Category | Description
Prefix segment | Identifies the prefix of a destination address on a network. Generation mode: manual configuration Prefix segments are propagated to other devices through an IGP. They are visible to and effective on all the devices. Node segments are special prefix segments.
Adjacency segment | Identifies an adjacency on a network. Generation mode: dynamic allocation by the ingress through a protocol Adjacency segments are propagated to other devices through an IGP. They are visible to all the devices but effective only on the local device.
R1
R2
R3
10.1.1.0/24
10.2.2.0/24
100
200
300
16001
16002
Loopback1
1.1.1.1/32
Loopback1
2.2.2.2/32
Loopback1
3.3.3.3/32
Node SID
Prefix SID
Adjacency SID
Note: SIDs are identified in the same way in the following parts.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 17: Basic Concept: Prefix Segment
R1
R2
R3
10.1.1.0/24
10.2.2.0/24
100
200
300
Prefix Segment
Identifies the prefix of a destination address on a network. Prefix segments are propagated to other devices through an IGP. They are visible to and effective on all the devices.
Prefix segments are identified using prefix SIDs.
A prefix SID is an offset value within the Segment Routing global block (SRGB) range advertised by the advertising end. The receiving end calculates the actual label value based on its own SRGB to generate an MPLS forwarding entry.
Loopback1
1.1.1.1/32
Loopback1
2.2.2.2/32
Loopback1
3.3.3.3/32
Node segments are special prefix segments used to identify specific nodes.
When an IP address is configured as a prefix for a node's loopback interface, the prefix SID of the node is the node SID.
16001
16002
Similar to the destination address in an IP route
Similar to the destination address in an IP route
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 18: Basic Concept: SRGB
Segment Routing global block (SRGB): a set of user-specified global labels reserved for SR-MPLS.
Each device advertises its SRGB through an extended routing protocol.
After a node advertises the prefix SID index through an extended routing protocol, each device receiving the index calculates the incoming and outgoing SIDs based on the SRGB.
In actual deployment, it is recommended that devices use the same SRGB.
Why is SRGB required?
  SR requires prefix SIDs to be globally valid.
  In MPLS, some label space of a device may be occupied by other protocols, such as LDP. Therefore, a specific space must be specified for global SR labels.
R1
R2
R3
Index
30
Loopback1
3.3.3.3/32
16000–17000
12000–13000
20000–21000
Incoming label
16000+30=16030
Incoming label
12000+30=12030
Incoming label
20000+30=20030
SRGB
SRGB
SRGB
12030
Payload
Swap
20030
Payload
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 19: Basic Concept: Adjacency Segment
R1
R2
R3
10.1.1.0/24
10.2.2.0/24
100
200
300
Adjacency Segment
Identifies an adjacency on a network. Adjacency segments are propagated to other devices through an IGP. They are visible to all the devices but effective only on the local device.
Adjacency segments are identified using adjacency SIDs.
Adjacency SIDs are local SIDs that are not in the SRGB range.
Loopback1
1.1.1.1/32
Loopback1
2.2.2.2/32
Loopback1
3.3.3.3/32
1001
1002
16001
16002
Similar to the outbound interface information in an IP route
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 20: Intra-AS Propagation of Node SIDs and Adjacency SIDs
SR-MPLS uses an IGP to advertise topology, prefix, SRGB, and label information. This is achieved by extending the TLVs of protocol packets for the IGP.
1001
1002
R1
R2
R3
10.1.1.0/24
10.2.2.0/24
100
200
300
16001
16002
Loopback1
1.1.1.1/32
Loopback1
2.2.2.2/32
Loopback1
3.3.3.3/32
Extended IGP
(e.g. IS-IS/OSPF)
Extended IGP
(e.g. IS-IS/OSPF)
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 21: OSPF for SR-MPLS
Name | Function | Carried In
SR-Algorithm TLV | Advertises the algorithm that is used. | Type 10 Opaque LSA
SID/Label Range TLV | Advertises the SR-MPLS SID or MPLS label range. | Type 10 Opaque LSA
SRMS Preference TLV | Advertises the priority of an NE functioning as an SR mapping server. | Type 10 Opaque LSA
SID/Label Sub-TLV | Advertises SR-MPLS SIDs or MPLS labels. | SID/Label Range TLV
 |  | OSPFv2 Extended Prefix TLV and OSPF Extended Prefix Range TLV in OSPFv2 Extended Prefix Opaque LSA
 |  | OSPFv2 Extended Link TLV in OSPFv2 Extended Link Opaque LSA
Prefix SID Sub-TLV | Advertises SR-MPLS prefix SIDs. | OSPFv2 Extended Prefix TLV and OSPF Extended Prefix Range TLV in OSPFv2 Extended Prefix Opaque LSA
Adj-SID Sub-TLV | Advertises SR-MPLS adjacency SIDs on a P2P network. | OSPFv2 Extended Link TLV in OSPFv2 Extended Link Opaque LSA
LAN Adj-SID Sub-TLV | Advertises SR-MPLS adjacency SIDs on a LAN. | OSPFv2 Extended Link TLV in OSPFv2 Extended Link Opaque LSA
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 22: IS-IS for SR-MPLS
Name | Function | Carried In
Prefix-SID Sub-TLV | Advertises SR-MPLS prefix SIDs. | IS-IS Extended IPv4 Reachability TLV-135 IS-IS Multitopology IPv4 Reachability TLV-235 IS-IS IPv6 IP Reachability TLV-236 IS-IS Multitopology IPv6 IP Reachability TLV-237 SID/Label Binding TLV
Adj-SID Sub-TLV | Advertises SR-MPLS adjacency SIDs on a P2P network. | IS-IS Extended IS reachability TLV-22 IS-IS IS Neighbor Attribute TLV-23 IS-IS inter-AS reachability information TLV-141 IS-IS Multitopology IS TLV-222 IS-IS Multitopology IS Neighbor Attribute TLV-223
LAN-Adj-SID Sub-TLV | Advertises SR-MPLS adjacency SIDs on a LAN. | IS-IS Extended IS reachability TLV-22 IS-IS IS Neighbor Attribute TLV-23 IS-IS inter-AS reachability information TLV-141 IS-IS Multitopology IS TLV-222 IS-IS Multitopology IS Neighbor Attribute TLV-223
SID/Label Sub-TLV | Advertises SR-MPLS SIDs or MPLS labels. | SR-Capabilities Sub-TLV and SR Local Block Sub-TLV
SID/Label Binding TLV | Advertises the mapping between prefixes and SIDs. | IS-IS LSP
SR-Capabilities Sub-TLV | Advertises SR-MPLS capabilities. | IS-IS Router Capability TLV-242
SR Local Block Sub-TLV | Advertises the range of labels reserved for local SIDs. | IS-IS Router Capability TLV-242
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 23: Basic Concept: SR Policy
According to RFC 8402, an SR Policy is an ordered list of segments. In addition, it defines a framework for SR technologies used to calculate/generate/maintain the segment list and steer traffic. Currently, SR Policy is the mainstream SR implementation mode.
Traffic is steered into an SR Policy by the headend. The involved segment list is accurately encapsulated as a label stack to guide traffic forwarding. It is calculated based on a series of optimization objectives and constraints, such as latency, affinity, and SRLG. The calculation can be performed locally or by a controller and then applied to the network.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 24: SR Policy Example
R1
R2
R3
10.1.1.0/24
10.2.2.0/24
100
200
300
SR Policy:
Can be generated using different modes, such as CLI, NETCONF, PCEP, and BGP SR Policy.
Contains segment lists to guide traffic steering and forwarding.
1012
1002
16001
16002
100
1012
1002
16002
SR Policy
1
Traffic steering
2
Tunnel-based forwarding
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 25: Basic Concept: SR-MPLS and SRv6
SR-MPLS
SRv6
R1
R2
R2
R3
MPLS
MPLS
MPLS
MPLS
Data forwarding plane: based on MPLS
MPLS labels are used as SIDs.
Segment list information is encoded as a label stack. The segment to be processed is at the stack top. Once a segment is processed, the corresponding label is removed from the label stack.
R1
R2
R2
R3
IPv6
IPv6
IPv6
IPv6
IP packet
MPLS packet
MPLS packet
Data forwarding plane: based on IPv6
IPv6 addresses are used as SIDs.
Segment list information is encoded as a label stack and carried using the IPv6 Segment Routing header (SRH).
IPv6 packet
IPv6 packet
IPv6 packet
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 26: Label Stack, Stitching Label, and Stitching Node
Label Stack
A label stack is an ordered set of labels used to identify a complete LSP.
Each adjacency label in the label stack identifies an adjacency, and the entire label stack identifies all adjacencies along the LSP.
During packet forwarding, a node searches for the corresponding adjacency according to each adjacency label in the label stack, removes the label, and then forwards the packet. After all the adjacency labels in the label stack are removed, the packet traverses the entire LSP and reaches the tunnel destination.
1013
R1
R2
R3
R4
R5
R6
1032
1024
1046
1013
1032
1024
1046
Stitching Label and Stitching Node
If the label stack depth exceeds the maximum depth supported by forwarders, the controller needs to allocate multiple label stacks to the forwarders and a special label to an appropriate node to stitch these label stacks, thereby implementing segment-by-segment forwarding.
This special label is called a stitching label, and this appropriate node is called a stitching node. The controller allocates a stitching label to the stitching node and pushes it to the bottom of the label stack.
1013
R1
R2
R3
R4
R5
R6
1032
1024
1056
1013
1032
100
1045
1024
1045
1056
100
Stitching label
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 27: How Are SIDs Used
Combining prefix (node) and adjacency SIDs in sequence can construct any network path.
Every hop on a path identifies the next hop based on the top SID in the label stack.
SID information is stacked in sequence at the top of the data header.
If the top SID identifies another node, the receive node forwards the data packet to that node in ECMP mode.
If the top SID identifies the local node, the receive node removes the top SID and proceeds with the follow-up procedure.
In real-world applications, prefix segments and adjacency segments can be used separately or together.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 28: Scenario 1: Prefix Segment-based Forwarding Path
Loopback1
2.2.2.2/32
Prefix SID=100
R2
Cost=1
Cost=1
Cost=1
Cost=1
Cost=10
Cost=10
Cost=10
Cost=10
R1
A prefix segment-based forwarding path is computed by an IGP using the SPF algorithm.
After the prefix SID (100) of R2 is propagated using an IGP, all devices in the IGP domain learn the SID.
R1 is used as an example (the implementation for other devices is similar to this). It runs SPF to compute the shortest path to R2.
Path with the minimum cost
Prefix segment-based forwarding paths are not fixed, and the ingress cannot control the entire packet forwarding path.
100
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 29: Scenario 2: Adjacency Segment-based Forwarding Path
Loopback1
2.2.2.2/32
R2
1023
R1
An adjacency segment is allocated to each adjacency on the network, and a segment list containing multiple adjacency segments is defined on the ingress.
This method can be used to specify any strict explicit path, facilitating SDN implementation.
1034
1056
1078
1023
1034
1056
1078
1034
1056
1078
1056
1078
1078
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 30: Scenario 3: Adjacency Segment+Node Segment-based Forwarding Path
R2
1023
R1
Adjacency and node segments can be used together. An adjacency segment can be specified to force a path to traverse an adjacency. The node corresponding to a node segment can run SPF to compute the shortest path that supports ECMP.
Paths established in this mode are not strictly fixed, and therefore, they are also called loose explicit paths.
1034
101
1034
100
1034
100
100
100
Loopback1
2.2.2.2/32
Prefix SID=100
Node SID=101
101
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 31: SR-MPLS BE
R4
R5
R1
R2
R3
SR-MPLS BE
In SR-MPLS best effort (BE) mode, SIDs are used to guide data forwarding over the shortest path.
In this example, node SID 606 of R6 is used to instruct data to be forwarded over the shortest path to R6. The shortest path is computed through a routing protocol and supports ECMP.
SR-MPLS BE is a new solution that replaces the LDP+IGP solution.
6.6.6.0/24
16002
R6
606
Packet
606
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 32: SR-MPLS TE
R4
R5
R1
R2
R3
SR-MPLS TE
In SR-MPLS TE mode, multiple SIDs are combined to guide data forwarding based on constraints, thereby meeting traffic engineering requirements.
Methods of combining SIDs:
  Combine multiple node SIDs.
  Combine multiple adjacency SIDs.
  Combine node and adjacency SIDs, as shown in the figure.
6.6.6.0/24
16002
R6
606
202
1025
Packet
606
1025
202
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 33: SR-MPLS BE LSP
An SR-MPLS BE LSP is a label forwarding path established using the SR technology. It uses a prefix or node segment to guide packet forwarding.
An SR-MPLS BE LSP is the optimal SR LSP computed by an IGP using the SPF algorithm.
The creation and data forwarding of SR-MPLS BE LSPs are similar to those of LDP LSPs. SR-MPLS BE LSPs do not have tunnel interfaces.
Loopback1
4.4.4.4/32
Prefix index 100
R1
R2
R3
R4
SRGB
20000-65535
SRGB
30000-65535
SRGB
40000-65535
SRGB
50000-65535
Advertise the prefix SID and SRGB
Advertise the prefix SID and SRGB
Advertise the prefix SID and SRGB
Incoming label 50100
Incoming label 40100
Outgoing label 50100
Incoming label 30100
Outgoing label 40100
Incoming label 20100
Outgoing label 30100
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 34: SR-MPLS BE LSP Creation
LSP creation involves the following operations:
  Network topology reporting (required only in controller-based LSP creation) and label allocation
  Path computation
SR-MPLS BE LSPs are created primarily based on prefix labels. Specifically, the destination node runs an IGP to advertise a prefix SID. After receiving the packet carrying the SID, forwarders parse the packet to obtain the SID and compute label values based on their own SRGBs. Then, using the IGP-collected topology information, each node runs the SPF algorithm to compute a label forwarding path, and delivers the computed next hop and outgoing label (OuterLabel) information to the forwarding table to guide data packet forwarding.
Loopback1
4.4.4.4/32
Prefix SID=100
R1
R2
R3
R4
SRGB
20000–65535
SRGB
30000–65535
SRGB
40000–65535
SRGB
50000–65535
Advertise the prefix SID and SRGB
Advertise the prefix SID and SRGB
Advertise the prefix SID and SRGB
Incoming label 50100
Incoming label 40100
Outgoing label 50100
Incoming label 30100
Outgoing label 40100
Incoming label 20100
Outgoing label 30100
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 35: Data Forwarding Process
Push: When a packet enters an LSP, the ingress adds a label between the Layer 2 and IP headers of the packet or adds a new label on top of the existing label stack.
Swap: After receiving a packet forwarded within the SR domain, a node uses the label allocated by the next hop to replace the top label according to the label forwarding table.
Pop: When a packet leaves the SR domain, the egress searches for the outbound interface according to the top label in the packet and then removes the top label.
Loopback1
4.4.4.4/32
Index 100
R1
R2
R3
R4
SRGB
20000–65535
SRGB
30000–65535
SRGB
40000–65535
SRGB
50000–65535
Packet
30100
Packet
40100
Packet
50100
Packet
Packet
Push
Swap
Swap
Pop
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 36: Traffic Engineering
Traffic engineering (TE) is one of the most important network services. The traditionally popular TE technology is based on MPLS and therefore is called MPLS TE. It can accurately control the path through which traffic passes, maximizing bandwidth utilization.
Path Planning
Traffic Optimization
Fault Protection
Different paths are planned for different services.
When traffic is unbalanced due to major events, traffic is evenly distributed to idle links.
A fast protection switching is performed in the case of a device or link fault.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 37: Traditional Distributed MPLS TE Architecture
MPLS TE uses the distributed architecture, in which the ingress computes paths according to constraints and uses RSVP-TE signaling to establish constraint-based LSPs.
MPLS nodes are used to maintain a complete TE architecture through four components: information advertisement component, path computation component, path establishment component (or signaling component), and packet forwarding component.
Network device
4. Packet forwarding component
1. Information advertisement component: IS-IS/OSPF
Path selection component
(IGP computation)
LSDB
2. Path selection component
(LSP computation)
TE database
3. Signaling component
(RSVP)
Packet leaving
Packet entering
Information advertisement
Information advertisement
LSP establishment
LSP establishment
The extended IS-IS/OSPF carries TE information, advertises IGP and TE information in the domain, and generates a TEDB.
The CSPF algorithm is used to compute a path that meets constraints based on the TEDB.
RSVP-TE is used to establish LSPs.
Data is forwarded based on MPLS labels.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 38: Centralized SR-MPLS TE Architecture
Segment Routing-MPLS Traffic Engineering (SR-MPLS TE) is a new TE tunneling technology that uses SR as the control protocol. SR-MPLS TE supports the centralized architecture, in which the controller collects global network topology and TE information, computes paths in a centralized manner, and delivers path computation results to network devices.
SR-MPLS TE also supports manual configuration.
Network device
4. Packet forwarding component
Information advertisement component: IS-IS/OSPF
Signaling component
Local TE database
Information reporting component
Packet leaving
Packet entering
Information advertisement
Information advertisement
Controller
3. Signaling component
(PCEP/BGP)
2. Centralized path computation component
Global TE database
1. Information collection component
(BGP-LS)
Centralized SR-MPLS TE:
The extended IS-IS/OSPF carries TE information, advertises IGP and TE information in the domain, and generates a TEDB.
BGP-LS is used to collect network information and establish a global TE database.
The controller globally computes paths based on constraints.
PCEP or BGP SR Policy is used to deliver path computation results to devices.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 39: Comparison Between SR-MPLS TE and RSVP-TE
Item | SR-MPLS TE | RSVP-TE
Label allocation | Labels are allocated and propagated using IGP extensions. Each link is allocated with only one label. All LSPs traversing a link share the label of this link, reducing label resource consumption and the workload in label forwarding table maintenance. | Labels are allocated and propagated using RSVP extensions. Each LSP is allocated with a label. When there are multiple LSPs, multiple labels need to be allocated to the same link, occupying a large number of label resources and increasing the workload of maintaining the label forwarding table.
Control plane | IGP extensions are used for signaling control, reducing the number of required protocols. | RSVP-TE needs to be used as the MPLS control protocol, complicating the control plane.
Scalability | As transit nodes are unaware of tunnels and use packets to carry tunnel information, they only need to maintain forwarding entries instead of tunnel state information, enhancing scalability. | Tunnel state information and forwarding entries need to be maintained, resulting in poor scalability.
Path adjustment and control | Transit nodes are unaware of tunnels. The service path can be controlled only by performing label operations on the packet sent from the ingress, eliminating the need of hop-by-hop configuration delivery. If a node in the path fails, the controller re-computes a path and updates the label stack of the ingress to complete path adjustment. | Configurations need to be delivered node by node regardless of whether the path is adjusted in normal or fault scenarios.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 40: SR-MPLS TE: Network Topology Collection
Network Topology Reporting Using BGP-LS
BGP-LS is used to report TE information and network topology information with SR labels to the controller.
R4
R5
R1
R2
R3
R6
IGP
IGP
Controller
BGP-LS
Network Topology Collection Using an IGP
The IGP configured on forwarders is used to collect network topology information, SR adjacency labels, and node labels.
R4
R5
R1
R2
R3
R6
IGP
IGP
Controller
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
IGP
Notes: For SR-capable IGP instances, all IGP-enabled outbound interfaces are allocated with SR adjacency labels, which are propagated to the entire network through an IGP.
In Huawei's early solutions, an IGP can also be used to collect network topology information. Due to IGP area-related restrictions, BGP-LS is mainly used at present.

## Slide 41: SR-MPLS TE: Label Allocation
In SR-MPLS TE, labels are allocated through the IGP configured on forwarders and reported to a controller through BGP-LS.
SR-MPLS TE mainly uses adjacency labels and can also use node labels.
Adjacency labels are allocated by the ingress, and are valid locally and unidirectional.
R4
R5
R1
R2
R3
R6
IGP
IGP
Controller
BGP-LS
1045
1054
GE0/0/1
GE0/0/2
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 42: Label Allocation Example
IGP SR is enabled on each device. For SR-capable IGP instances, all IGP-enabled outbound interfaces are allocated with SR adjacency labels.
Adjacency labels are propagated to the entire network through an IGP SR extension.
Taking R4 as an example, the process of label allocation through an IGP is as follows:
  R4 allocates a local dynamic label to an adjacency through an IGP. For example, adjacency label 1045 is allocated to the R4->R5 adjacency.
  R4 propagates the adjacency label to the entire network through the IGP.
  R4 generates a label forwarding entry corresponding to the adjacency label.
  Other nodes learn the R4-propagated adjacency label through the IGP but do not generate label forwarding entries.
Other devices allocate and propagate adjacency labels in the same way as R4 and generate label forwarding entries. BGP-LS is used to report TE information and network topology information with SR labels to the controller.
R4
R5
R1
R2
R3
R6
IGP
IGP
Controller
BGP-LS
1045
1054
GE0/0/1
GE0/0/2
Label | Outbound Interface | Next Hop
1045 | GE0/0/1 | R5
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 43: SR-MPLS TE LSP Creation
SR-MPLS TE tunnels are created using the SR protocol based on TE constraints. The figure shows two LSPs working in primary/backup mode. The two LSPs correspond to the same SR-MPLS TE tunnel with a specified ID.
R2
R1
Path 1: primary path
Path 2: backup path
SR-MPLS TE tunnel creation involves tunnel attribute configuration and tunnel establishment.
SR-MPLS TE tunnel
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: Before SR-MPLS TE tunnel creation, IS-IS/OSPF neighbor relationships must be established between forwarders to implement network layer connectivity, allocate labels, and collect network topology information. In addition, the forwarders need to report label and network topology information to a controller for path computation. If no controller is available, CSPF can be enabled on the ingress of the SR-MPLS TE tunnel so that forwarders can compute paths using CSPF.

## Slide 44: SR-MPLS TE Tunnel Attribute Configuration
SR-MPLS TE tunnel attributes must be configured before tunnel establishment. An SR-MPLS TE tunnel can be configured on a controller or forwarder.
Tunnel configuration on a controller: After an SR-MPLS TE tunnel is configured on a controller, the controller uses NETCONF to deliver tunnel attributes to a forwarder, which then uses PCEP to delegate the tunnel to the controller for management.
Tunnel configuration on a forwarder: After an SR-MPLS TE tunnel is configured on a forwarder, the forwarder delegates the tunnel to the controller for management.
[R1] interface tunnel1
[R1-Tunnel1] ip address unnumbered interface LoopBack0
[R1-Tunnel1] tunnel-protocol mpls te
[R1-Tunnel1] destination 3.3.3.3
[R1-Tunnel1] mpls te tunnel-id 1
[R1-Tunnel1] mpls te signal-protocol segment-routing
[R1-Tunnel1] mpls te pce delegate # The tunnel is delegated to the PCE server.
SR-MPLS TE tunnels are established and managed using tunnel interfaces. As such, you need to configure a tunnel interface on the ingress of each SR-MPLS TE tunnel.
NETCONF-based Tunnel Configuration Delivery by a Controller
[R1] interface tunnel1
[R1-Tunnel1] ip address unnumbered interface LoopBack0
[R1-Tunnel1] tunnel-protocol mpls te
[R1-Tunnel1] destination 3.3.3.3
[R1-Tunnel1] mpls te tunnel-id 1
[R1-Tunnel1] mpls te signal-protocol segment-routing
[R1-Tunnel1] mpls te path explicit-path p1 # A path is manually specified.
Manual Configuration of a Tunnel with an Explicit Path
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: For SR-MPLS TE tunnel configuration on a forwarder, in addition to manually specifying an explicit path, you can also use the function of path computation by the ingress.

## Slide 45: SR-MPLS TE Tunnel Establishment (Path Computation by the Controller)
Controller
BGP-LS
If a configured service (e.g. VPN service) needs to be bound to an SR-MPLS TE tunnel, the tunnel can be established as follows:
Based on SR-MPLS TE tunnel constraints, the controller uses the path computation element (PCE) to compute a path similar to a common TE tunnel and generates a label stack (path computation result).
The controller uses NETCONF and PCEP to deliver tunnel configurations and the tunnel stack, respectively, to forwarders.
The forwarders establish an SR-MPLS TE tunnel with a specific LSP based on the tunnel configurations and label stack delivered by the controller.
R2
1023
R1
1034
1056
1078
1023
1034
1056
1078
1034
1056
1078
1056
1078
1078
NETCONF
PCEP
BGP-LS: used to report labels and network topology information by forwarders.
PCEP: used to deliver a label stack by a controller and report LSP states by forwarders.
NETCONF: used to deliver tunnel configurations by a controller.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 46: Advantages of Controller-based SR-MPLS TE Tunnel Establishment
High bandwidth
Low latency
NETCONF
PCEP
PCEP
High-bandwidth path
Low-latency path
Controller
Bandwidth calculation and resource reservation are supported.
The optimal path can be computed from a global perspective.
The controller can work with applications. After applications raise network requirements, the controller can compute forwarding paths as required, achieving a service-driven network.
The workload of manual configuration is reduced, facilitating large-scale network deployment.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Data download
Video

## Slide 47: SR-MPLS TE Data Forwarding
Forwarders perform label operations on packets according to the label stacks corresponding to a specific SR-MPLS TE tunnel's LSP and search for outbound interfaces hop by hop according to the top label to guide packet forwarding to the destination. Data can be forwarded based on adjacency labels or a combination of node and adjacency labels.
Forwarding based on adjacency labels
  Forwarding based on adjacency labels is also called strict-path forwarding. The label stack strictly determines the forwarding path and does not support load balancing.
Forwarding based on a combination of node and adjacency labels
  Forwarding based on a combination of node and adjacency labels is also called loose-path forwarding. When processing node labels, a device can forward packets along the shortest path or perform load balancing because the path is not strictly fixed in this case.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: Currently, the mainstream solution is strict-path forwarding based on adjacency labels.

## Slide 48: SR-MPLS BE and SR-MPLS TE Traffic Steering
Traffic steering: After an SR tunnel is established, service traffic needs to be steered to it.
SR-MPLS BE (without tunnel interfaces) traffic steering
  Tunnel policy: Use a tunnel type prioritizing policy to select an SR-BE tunnel.
  Static route: Specify the next hop of a static route as the destination address of an SR-BE tunnel and recurse traffic to the tunnel based on the next hop.
  Recursion based on the next hop of a route: Recurse a public network route (e.g. BGP route) to an SR-BE tunnel based on the route's next hop.
SR-MPLS TE (with tunnel interfaces) traffic steering
  Tunnel policy: Use a tunnel type prioritizing policy to select an SR-TE tunnel.
  Static route: When configuring a static route, specify the outbound interface of the route as an SR-TE tunnel interface.
  Auto route: Use an SR-TE tunnel as a logical link in IGP route calculation.
  Policy-based routing (PBR): Specify an SR-TE tunnel interface as an outbound interface in the involved clause.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 49: SR-MPLS TE Disadvantages in the Early Stage
SR-MPLS TE in the early stage inherits the tunnel interface concept of RSVP-TE and uses tunnel interfaces to implement SR.
[R1] interface tunnel1
[R1-Tunnel1] ip address unnumbered interface LoopBack0
[R1-Tunnel1] tunnel-protocol mpls te
[R1-Tunnel1] destination 3.3.3.3
[R1-Tunnel1] mpls te tunnel-id 1
[R1-Tunnel1] mpls te signal-protocol segment-routing
...
Using tunnel interfaces to implement SR is simple and easy to understand, but has the following disadvantages:
  Tunnel interfaces and traffic steering are implemented separately, leading to complex traffic steering and low performance.
  Tunnels need to be configured and deployed in advance, imposing a restriction in scenarios where the tunnel destination cannot be determined.
  The application scenarios of tunnel interface-based ECMP are limited.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 50: SR Policy Overview
An SR Policy uses a segment list to specify a forwarding path, without the need to use tunnel interfaces.
SR Policies are classified into SR-MPLS Policies and SRv6 Policies based on segments. This document focuses on SR-MPLS Policies.
The controller computes paths based on the color attribute that represents SLAs and delivers the computation results to forwarders to form SR-MPLS Policies. (In this example, the forwarder's tunnel information is different from SR-TE tunnel information.) According to the color attribute and next hop of the involved service route, the headend recurses the route to the corresponding SR-MPLS Policy for service forwarding.
<PE1>display tunnel-info all
Tunnel ID Type Destination Status
----------------------------------------------------------------------------------------
0x0000000001004c4c04 ldp 1.0.0.12 UP
0x000000002900000004 srbe-lsp 1.0.0.12 UP
0x000000000300002001 sr-te 1.0.0.12 UP
0x00000000320000c001 srtepolicy 1.0.0.12 UP
0x000000003400002001 srv6tepolicy FC01::12 UP
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: https://datatracker.ietf.org/doc/draft-ietf-spring-segment-routing-policy/
An SR Policy is a framework that enables instantiation of an ordered list of segments on a node for implementing a source routing policy with a specific intent for traffic steering from that node.

## Slide 51: SR-MPLS Policy Tuple
An SR-MPLS Policy is identified by the tuple <headend, color, endpoint>.
For an SR-MPLS Policy with a specified node, it is identified only using <color, endpoint>.
  Headend: node where an SR-MPLS Policy is originated. Generally, it is a globally unique IP address.
  Color: 32-bit extended community attribute. It is used to identify a service intent (e.g. low latency).
  Endpoint: destination address of an SR-MPLS Policy. Generally, it is a globally unique IP address.
Color and endpoint are used to identify a forwarding path on the specific headend of an SR-MPLS Policy.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 52: SR-MPLS Policy Standards
According to RFC draft-ietf-spring-segment-routing-policy, BGP multi-protocol extension supports the BGP SR Policy (SAFI = 73) address family for delivering SR-MPLS Policies:
BGP-LS/BGP SR Policy
Controller
The controller uses BGP to deliver a combination of SR SIDs to the ingress. A TE tunnel carrying the policy color and destined for the egress is then created on the ingress.
If the tunnel needs to be referenced, you can locate the tunnel based on the policy color.
Color
Ingress
Egress
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: There are three mainstream methods for SR Policy implementation.
  BGP: BGP-LS is used to collect topology information, so that no new interface protocol needs to be introduced for customer-developed controllers. BGP SR Policy is used to deliver route information.
  PCEP: PCEP is a mature southbound protocol used in SR-MPLS TE scenarios. However, the tunnel implementation models of vendors are different and cannot interwork, and the interaction process of PCEP is more complex than that of BGP. As such, BGP extension is recommended.
  NETCONF/YANG: delivers tunnel paths to forwarders as configurations. This method is not recommended because it delivers configurations in essence and offers the poorest performance. In a comprehensive solution, NETCONF is used to deliver configurations other than tunnel configurations.
For details about SR Policy, see [I-D.ietf-spring-segment-routing-policy]. (https://datatracker.ietf.org/doc/draft-ietf-idr-segment-routing-te-policy/)

## Slide 53: SR-MPLS Policy Solution Architecture
1. BGP-LS
Controller
Color
Ingress
Egress
2. BGP SR Policy
3. NETCONF
Huawei SR-MPLS Policy solution architecture involves three key protocols: BGP-LS, BGP SR Policy, and NETCONF.
  BGP-LS collects information (e.g. tunnel topology, bandwidth, and link latency) and reports it to the controller, which then computes SR Policy paths and displays tunnel status based on the information.
  BGP SR Policy is used by the controller to deliver SR Policy information (e.g. color, headend, and endpoint).
  NETCONF is used to deliver other configurations, such as service interfaces and route-policies (with the color attribute).
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: BGP-LS connection:
  Collects tunnel topology information for SR Policy path computation.
  BGP-LS supports the collection of SR Policy status information, based on which the controller displays tunnel status. https://datatracker.ietf.org/doc/draft-ietf-idr-te-lsp-distribution/
  BGP-LS supports SRLB information encapsulation and decapsulation, so that the controller can obtain the SRLB information for binding SID allocation. (The backup path of each SR Policy corresponds to a binding SID.)
BGP SR Policy connection:
  The controller delivers SR Policy information to forwarders to generate SR Policies.
  BGP routes delivered by the controller carry the color community attribute, and this attribute can be transmitted. The ingress finds a matching BGP route and recurses it to an SR Policy based on the color and endpoint information.
  In the SR Policy solution, path computation constraints of each application need to be planned in a unified manner on the controller based on SLAs, different colors are used to identify SR Policies. An SR Policy is uniquely identified by <headend, color, endpoint>. The BGP route of services to be steered into an SR Policy needs to carry the corresponding color attribute.
Huawei SR-MPLS Policy solution also uses PCEP for tunnel status query.

## Slide 54: SR-MPLS Policy Model
An SR-MPLS Policy can contain multiple candidate paths with the preference attribute. The valid candidate path with the highest preference functions as the primary path of the SR-MPLS Policy, and the valid candidate path with the second highest preference functions as the backup path.
A candidate path is an SR-MPLS Policy's segment list sent to the headend through PCEP or BGP SR Policy.
SR Policy
Candidate path 1
Preference 200
Candidate path 2
Preference 100
Segment list 1
Weight
Segment list 2
Weight
Segment list 1
Weight
Primary path
Backup path
SR policy P1 <headend, color, endpoint>
Candidate-path CP1 <protocol, origin, discriminator>
Preference 200
Weight W1, SID-List1 <SID11...SID1i>
Weight W2, SID-List2 <SID21...SID2j>
Candidate-path CP2 <protocol, origin, discriminator>
Preference 100
Weight W3, SID-List3 <SID31...SID3i>
Weight W4, SID-List4 <SID41...SID4j>
<headend, color, endpoint>
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: An SR Policy can contain multiple candidate paths (e.g. CP1 and CP2). Each of the paths is uniquely determined by the triplet <protocol, origin, discriminator>.
CP1 is the primary path because it is valid and has the highest preference. The two SID lists of CP1 are delivered to the forwarder, and traffic is balanced between the two paths based on weights. For SID-List <SID11...SID1i>, traffic is balanced according to W1/(W1+W2). In the current mainstream implementation, a candidate path has only one segment list.

## Slide 55: Binding SID
To achieve better scalability, network opacity, and service independence, the binding SID (BSID) mechanism is introduced to SR. (RFC 8402-5.Binding Segment) A BSID can be defined for each candidate path.
Similar to RSVP-TE tunnels, SR-MPLS TE tunnels can also function as forwarding adjacencies. If an SR-MPLS TE tunnel is used as a forwarding adjacency and an adjacency SID is allocated to it, this SID is called a BSID. A BSID identifies an SR-MPLS TE tunnel.
sr-te policy P1
binding-sid 200
endpoint 5.5.5.5 color 100
Static BSID Configuration
Only one BSID can be configured for an SR-MPLS Policy. It can be used for SR-MPLS TE path computation as other types of SIDs.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: Source of BSIDs: SRLB or SRGB
Each candidate path of an SR Policy has a BSID. The BSIDs of different candidate paths of the same SR Policy are generally the same. The BSIDs of different SR Policies must be different. Generally, the BSID range needs to be planned and cannot be shared with other services.
The headend of an SR Policy forwards packets over the SR Policy based on the BSID. For example, when the headend receives a packet carrying a BSID, it uses the corresponding SR Policy to forward the packet.
BSIDs are used in label-based traffic steering scenarios, especially label stitching scenarios and tunnel protocol interworking scenarios, such as LDP over SR.
For details, see draft-ietf-spring-segment-routing-policy-6.Binding SID.

## Slide 56: SR-MPLS Policy Service Process: Information Collection
Controller
Green
R1:
Ingress
R3:
Egress
BGP-LS collects information (e.g. topology, bandwidth, and link latency) and reports it to the controller, which then computes SR Policy paths and displays tunnel status based on the information.
BGP-LS
3.3.3.3
20003
1.1.1.1
20001
Prefix: 5.5.5.5/32
2.2.2.2
20002
4.4.4.4 20004
Background: R3 functions as the egress and advertises the route 5.5.5.5/32 to the ingress R1. Finally, an SR Policy is established between R1 and R3. The figure shows the associated path. The specified color is green.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: Preparations:
  Controller planning: You can plan the color attribute and the mapping between the color attribute and SR tunnels' SLA requirements (path computation constraints) on the controller based on the SLA requirements of services.
  Enable SR on involved devices.
  Create a BGP session between the ingress and egress to advertise BGP VPN route information.
  Check that the BGP peer relationship is established successfully and a reachable route carrying the color attribute exists between the ingress and egress.

## Slide 57: SR Policy Service Process: Route Coloring
Controller
Green
R1:
Ingress
R3:
Egress
The controller uses NETCONF to deliver a VPN or BGP export route-policy to the egress. The color attribute (green) is set for the route prefix 5.5.5.5/32, and the next hop of the route is R3 address 3.3.3.3.
NETCONF
3.3.3.3
20003
1.1.1.1
20001
Prefix: 5.5.5.5/32
Color: Green
NHP: 3.3.3.3
2.2.2.2
20002
4.4.4.4 20004
Background: R3 functions as the egress and advertises the route 5.5.5.5/32 to the ingress R1. Finally, an SR Policy is established between R1 and R3. The figure shows the associated path. The specified color is green.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 58: SR Policy Service Process: Route Advertisement
Controller
Green
R1:
Ingress
R3:
Egress
The egress advertises the colored route 5.5.5.5/32 to the ingress through MP-BGP.
3.3.3.3
20003
1.1.1.1
20001
Prefix: 5.5.5.5/32
Color: Green
NHP: 3.3.3.3
2.2.2.2
20002
4.4.4.4 20004
MP-BGP
Background: R3 functions as the egress and advertises the route 5.5.5.5/32 to the ingress R1. Finally, an SR Policy is established between R1 and R3. The figure shows the associated path. The specified color is green.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals

## Slide 59: SR Policy Service Process: SR Policy Delivery
Controller
Green
R1:
Ingress
R3:
Egress
The controller delivers the SR Policy to the headend, as shown in the following. R1 receives the BGP route 5.5.5.5/32 from R3. In subsequent forwarding, the route is recursed to the SR Policy based on its color and next hop.
BGP SR Policy
3.3.3.3
20003
1.1.1.1
20001
Prefix: 5.5.5.5/32
Color: Green
NHP: 3.3.3.3
2.2.2.2
20002
4.4.4.4 20004
SR Policy:
Color: Green
Tunnel Encap
...
SR Policy:
Color: Green
Endpoint: 3.3.3.3
Attribute:
BSID: 30028
Candidate path count: 1
Preference:100 SegmentList:
label: 20004, 20003
BGP SR Policy Route:
Background: R3 functions as the egress and advertises the route 5.5.5.5/32 to the ingress R1. Finally, an SR Policy is established between R1 and R3. The figure shows the associated path. The specified color is green.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: The steps in this document do not represent the actual configuration sequence. They are only used to help you understand the implementation process. In real-world situations, the controller may deliver SR Policies and use NETCONF to deliver configurations at the same time.

## Slide 60: SR Policy Service Process: Traffic Steering and Packet Forwarding
Controller
Green
R1:
Ingress
R3:
Egress
The ingress generates a forwarding-plane tunnel based on the SR Policy. In this example, it completes traffic steering and forwarding based on the color attribute.
Other traffic steering modes, such as DSCP-based traffic steering, are also supported.
BGP SR Policy
3.3.3.3
20003
1.1.1.1
20001
Prefix: 5.5.5.5/32
Color: Green
NHP: 3.3.3.3
2.2.2.2
20002
4.4.4.4 20004
Background: R3 functions as the egress and advertises the route 5.5.5.5/32 to the ingress R1. Finally, an SR Policy is established between R1 and R3. The figure shows the associated path. The specified color is green.
SR Policy:
Color: Green
Tunnel Encap
...
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: DSCP-based traffic steering does not support color-based route recursion. Instead, it recurses a route to an SR-MPLS Policy based on the next-hop address in the route. Specifically, it searches for the SR-MPLS Policy group matching specific endpoint information and then finds the corresponding SR-MPLS Policy based on the DSCP value of packets. For details, see the corresponding product documentation.

## Slide 61: Summary: SR-MPLS Path Generation Modes
SR is a technology that allows route selection on the ingress without depending on hop-by-hop signaling exchange (LDP/RSVP-TE). SR-MPLS paths are composed of segments advertised through an IGP. SR-MPLS paths support the following generation modes:
  Forwarder-based path computation (SPF/CSPF)
  Static explicit path configuration (CLI/NETCONF)
  Controller-based path computation (PCEP/BGP SR Policy)
Currently, BGP SR Policy is the mainstream path delivery mode.
SR-MPLS Policy
Basic Concept
SR-MPLS TE
SR-MPLS BE
Fundamentals
Notes: Path Computation Element Communication Protocol (PCEP) Extensions for SR: https://datatracker.ietf.org/doc/rfc8664/?include_text=1

## Slide 62
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing

## Slide 63: Overview of SR-MPLS Protection Technologies
TE tunnel protection is classified into local protection and E2E protection. These protection mechanisms are inherited and also enhanced for SR-MPLS TE.
Local protection
E2E protection
Ingress
Egress
Ingress
Egress
Fast switching
Only links and nodes protected
Detection-dependent fast switching
E2E paths protected
TI-LFA FRR
Hot Standby
Anycast FRR
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 64: TI-LFA FRR
Topology-independent loop-free alternate (TI-LFA) FRR provides link and node protection for SR tunnels. If a link or node fails, traffic is rapidly switched to the backup path.
Limitations of the Traditional LFA Algorithm
R1
R2
R3
R4
SIP: 1.1.1.1
DIP: 4.4.4.4
Cost=10
Cost=10
Cost =10
Cost =100
The traditional LFA algorithm has topological limitations. As shown in the figure, SIP traffic is forwarded to the DIP through R1. If the R1-R3 link fails, R1 forwards the traffic to R2. However, no backup path can be formed before R2 detects the failure.
TI-LFA Algorithm
R1
R2
R3
R4
SIP: 1.1.1.1
DIP: 4.4.4.4
Cost=10
Cost=10
Cost =10
Cost =100
Using the source routing capability of SR, TI-LFA computes a backup path on each node to protect the failure point. When a node detects a failure, traffic is rapidly switched to the backup path.
Primary R1-R3 path: 4.4.4.4; segment list: R1, R3
Backup R1-R3 path: 4.4.4.4; segment list: R1, R2, R4, R3
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: In a distributed network architecture, each device independently computes a path, and there is no consensus on the shortest path when a fault occurs. As a result, a backup path cannot be formed using traditional LFA.

## Slide 65: TI-LFA FRR Protection Path Computation
TI-LFA FRR protects services against both link and node failures. TI-LFA preferentially computes a node protection path because this path can definitely protect services against a link failure.
R1
R2
SIP: 1.1.1.1
DIP: 4.4.4.4
R3
R4
Original path
Protection path
Link protection
R1
R2
SIP: 1.1.1.1
DIP: 4.4.4.4
R3
R4
Original path
Protection path
Node protection
High priority
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: For details about TI-LFA FRR, see the "TI-LFA FRR" section in NE series product documentation.

## Slide 66: TI-LFA FRR Usage Scenarios and Configuration
To protect the entire path, you need to enable TI-LFA FRR local protection for the IGP processes of multiple nodes.
IS-IS 1 Level-2
[Router] isis 1
[Router-isis-1] frr
[Router-isis-1-frr] loop-free-alternate level-2
[Router-isis-1-frr] ti-lfa level-2
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 67: Limitations of TI-LFA FRR
TI-LFA cannot provide protection if a specified explicit node (ingress, egress, or constraint node) along an SR tunnel fails. For example, on the SR path shown in the following figure, TI-LFA cannot generate protection paths for explicit nodes R1, R4, and R6.
R1
16006
R2
R3
R5
R4
R6
16004
Packet
16001
16003
16005
TI-LFA cannot protect services against explicit node failures.
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
16002
16004
16006

## Slide 68: Anycast FRR
Anycast FRR can protect services against failures of specified nodes.
Assume that R4 and R5 advertise the same SID. This SID is called an anycast SID. The anycast SID is advertised in the IGP, with the next hop pointing to the nearest node on the path, such as R4. In this case, R4 is the optimal node of the anycast SID, and R5 is the backup node.
R1
R2
R3
R5
R4
R6
16001
16002
16100
16006
16003
Set the same SID (anycast SID) for different devices.
Optimal node
Backup node
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 69: Anycast FRR Protection
Anycast FRR constructs a virtual node for SID advertisement and uses the TI-LFA algorithm to compute the backup next hop of the virtual node.
If R4 fails, TI-LFA continues to forward traffic through R5 along the computed backup path.
R1
R2
R3
R5
R4
R6
16001
16002
16006
16003
Virtual node
16006
16100
Packet
16100
Backup path
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: The cost values of the links from R4 and R5 to the virtual node are both 0. However, the cost values of the links from the virtual node to R4 and R5 are infinite.

## Slide 70: Hot Standby
SR hot standby enables the controller to compute a backup path that is different from the primary path to implement E2E path protection.
For SR-MPLS Policies, the primary and backup candidate paths implement hot standby protection. The primary and backup candidate paths belong to the same SR-MPLS Policy.
PE1
P1
P3
P4
P2
PE2
16001
16002
16004
16006
16003
16005
PE3
16007
CE1
CE2
Backup candidate path
Primary candidate path
SR-MPLS Policy
Candidate path 1
Candidate path 2
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 71: Hot Standby Implementation for SR-MPLS Policy
SR-MPLS Policy
Candidate path 1
Preference 200
Candidate path 2
Preference 100
Segment list
Segment list
Primary candidate path
Backup candidate path
SR policy P1 <headend, color, endpoint>
Candidate-path CP1 <protocol, origin, discriminator>
Preference 200
SID-List <SID11...SID1i>
Candidate-path CP2 <protocol, origin, discriminator>
Preference 100
SID-List <SID21...SID2i>
<headend, color, endpoint>
Multiple candidate paths of an SR-MPLS Policy implement hot standby protection. If a segment list fails, a failover is triggered.
SR-MPLS Policy fault detection depends on detection mechanisms such as BFD or SBFD.
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 72: Limitations of Hot Standby
Hot standby can protect E2E paths but does not apply to scenarios where the egress PE of a tunnel fails. In this example, PE1 receives the routes advertised by PE2 and PE3 at the same time and preferentially selects the route advertised by PE2. If PE2 fails, services can recover only through route convergence.
PE1
P1
P3
P4
P2
PE2
16001
16002
16004
16006
16003
16005
PE3
16007
CE1
CE2
Primary candidate path
SR-MPLS Policy
Candidate path 1
Candidate path 2
Backup candidate path
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 73: VPN FRR
VPN FRR uses the VPN route-based fast switching technology. It presets primary and backup forwarding paths pointing to the master and backup PEs, respectively, on the ingress PE and implements fast PE failure detection to reduce E2E service convergence time when a PE failure occurs in an MPLS VPN scenario where a CE is dual-homed to two PEs.
PE1
P1
P3
P4
P2
PE2
16001
16002
16004
16006
16003
16005
PE3
16007
CE1
CE2
Backup candidate path of SR-MPLS Policy 1
Primary candidate path of SR-MPLS Policy 1
VPN FRR backup path (SR-MPLS Policy 2)
SR-MPLS Policy 1
Candidate path 1
Candidate path 2
SR-MPLS Policy 2 -
Candidate path 1
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: In traditional TE tunnel protection technologies, if a PE fails, services can recover only through E2E route convergence and LSP convergence. The service convergence time is closely related to the number of internal MPLS VPN routes and the number of hops on the bearer network. The greater the number of VPN routes, the longer the service convergence time.
In VPN FRR, service convergence time depends on only the time required to detect remote PE failures and change tunnel status, making service convergence time irrelevant to the number of VPN routes on the bearer network.
In this example, VPN FRR primary and backup paths exist from PE1 to PE3. They are not all displayed in the figure.

## Slide 74: VPN FRR Failover Example
In this example, when TI-LFA FRR, hot standby, and VPN FRR are used together, the protection switching is implemented as follows:
SR-MPLS Policy 1
Candidate path 1
Candidate path 2
SR-MPLS Policy 2 --
Candidate path 1
VPN FRR
16002
16004
16006
Segment list
TI-LFA FRR
Hot Standby
VPN FRR
16003
16005
16004
16003
16005
16007
16006
16003
160042
TI-LFA
PE1-P1 link on the protection path
If a node or link on the primary path fails, traffic is switched to the backup path.
If PE2 fails, SR-MPLS Policy 1 becomes unavailable, triggering VPN FRR switching to SR-MPLS Policy 2.
Note: Candidate path 1 of SR-MPLS Policy 1 is the primary path.
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: Fault detection in hot standby and VPN FRR scenarios depends on detection mechanisms such as BFD or SBFD.

## Slide 75: SR Microloop Avoidance Overview
Each node independently calculates the IGP LSDB, which may lead to a loop during unordered convergence. This may in turn result in microloops, a kind of transient loop that disappears after all the nodes on the forwarding path have converged.
On the network shown in the following figure, TI-LFA FRR is working properly. After detecting that P2 fails, P1 enters the TI-LFA FRR switching process. Specifically, it inserts the repair list <16005, 16057> into the packet to forward the packet to 16006 through 16005.
PE1
P1
P3
P4
P2
PE2
16001
16002
16004
16006
16003
16005
PE3
16007
TI-LFA
16057
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 76: SR Local Microloop Avoidance in a Traffic Switchover Scenario
Devices converge at different time points, leading to a microloop. For example, the route of P1 does not carry a repair list after convergence. In this case, the next hop of the route to 16006 is P3. If P3 has not converged, the next hop pointing to 16006 is still P1, causing a local microloop in a traffic switchover scenario.
After microloop avoidance is enabled, P1 starts the T1 timer during which the packet is still forwarded according to the TI-LFA policy <16005, 16057> and waits for other nodes to converge.
PE1
P1
P3
P4
P2
PE2
16001
16002
16004
16006
16003
16005
PE3
16007
[P1] isis 1
[P1-isis-1] avoid-microloop frr-protected
Converged
Not converged
16057
TI-LFA
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 77: SR Local Microloop Avoidance in a Traffic Switchback Scenario
A microloop may also occur during traffic switchback implemented after fault rectification. Assume that P2 recovers. If P1 has not converged and forwards traffic to P3 that has converged, traffic will be forwarded back to P1, resulting in a local microloop.
With microloop avoidance enabled, after P3 converges, it computes the microloop avoidance segment list <16002, 16024>. PE1 forwards the packet to P1. As P1 has not converged, it forwards the packet to P3. P3 inserts the segment list into the packet and forwards the packet to P2 through P1 and finally to PE2.
PE1
P1
P3
P4
P2
PE2
16002
PE3
TI-LFA
Converged
Not converged
16024
[P3] isis 1
[P3-isis-1] avoid-microloop frr-protected
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
16001
16004
16006
16003
16005
16007

## Slide 78: SR Remote Microloop Avoidance
Traffic switching may cause not only a local microloop but also a microloop between remote nodes (that is, a remote microloop).
As shown in the figure, the link between PE2 and PE3 fails. If P2 has converged but P1 has not, a loop occurs between P1 and P2.
With remote microloop avoidance enabled, after P2 converges, it computes the microloop avoidance segment list <16003,16037> for traffic accessing PE3. In this case, P1 still forwards traffic from P3 to PE3 even if P1 has not converged.
PE1
P1
P3
P2
PE2
16002
16004
16006
16003
PE3
16007
16037
[P2] isis 1
[P2-isis-1] avoid-microloop segment-routing
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
16001

## Slide 79: Summary: Comparison Between TI-LFA and Microloop Avoidance
TI-LFA
Microloop Avoidance
Purpose: to locally compute a backup path for the destination address.
Trigger condition: link or node failure on the primary path.
Purpose: to prevent temporary loops during the update of the primary path.
Trigger condition: primary path update.
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 80: SBFD Overview
If BFD detects a large number of links, the negotiation time of the state machine is prolonged, which is not suitable for SR. To address this issue, seamless bidirectional forwarding detection (SBFD), which is a simplified BFD mechanism, is introduced to detect SR tunnels. With a simplified BFD state machine, SBFD shortens the negotiation time and improves network-wide flexibility.
BFD negotiation
Down
Down -> Init
Down -> Up
Down
Down -> Init
Down -> Up
BFD Down
BFD Init
BFD Up
BFD Down
BFD Init
BFD Up
SBFD negotiation
Down
Down -> Up
Initiator
Initiator
Initiator
Reflector
BFD Down
BFD Down
Reflection only
Multiple initiators share one reflector.
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 81: SBFD Implementation
Initiator
Reflector
SBFD Control Packet
SBFD Control Packet
Down
Down -> Up
SBFD Echo Packet
During link detection
Before link detection
Before link detection, both ends exchange SBFD control packets to notify SBFD description information.
During link detection, the initiator proactively sends an SBFD Echo packet, and the reflector loops back the packet based on local conditions. The initiator determines the local status based on the reflected packet.
Down
Up
Up
Admin Down
(Timer)
Admin Down
(Timer)
Up
The loopback packet constructed by the reflector carries the Admin Down or Up field.
After receiving a reflected packet carrying the Up state, the initiator sets the local state to Up. After receiving a reflected packet carrying the Admin Down state, it sets the local state to Down. It also sets the local state to Down if it does not receive any reflected packet before the timer expires.
SBFD state machine of the initiator
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD
Notes: Because the state machine has only Up and Down states, the initiator can send packets carrying only the Up or Down state and receive packets carrying only the Up or Admin Down state. The initiator starts by sending an SBFD packet carrying the Down state to the reflector. The destination and source port numbers of the packet are 7784 and 4784, respectively; the destination IP address is a user-configured address on the 127 network segment; the source IP address is the locally configured LSR ID.
The reflector runs no SBFD state machine or detection mechanism. For this reason, it does not proactively send SBFD Echo packets. Instead, it only reflects back received SBFD packets. The destination and source port numbers in the looped-back SBFD packet are 4784 and 7784, respectively; the source IP address is the locally configured LSR ID; the destination IP address is the source IP address of the initiator.

## Slide 82: One-Arm BFD
BFD/SBFD requires that devices at both ends support this function. If a Huawei device needs to communicate with a BFD-incapable device, you can configure one-arm BFD (also called one-arm BFD echo) for the Huawei device. A one-arm BFD Echo session can be established on the BFD-capable device. After receiving a BFD Echo packet, the BFD-incapable device immediately loops back the packet for quick link detection.
One-arm BFD Echo does not require Echo negotiation capabilities at both ends; that is, BFD can be configured on only one end. The device with one-arm Echo enabled sends special BFD packets (source and destination IP addresses in the IP header are the IP address of the local device, and the local and remote discriminators in the BFD packet are the same). After receiving the packets, the peer device directly loops them back to the local device to check whether the link is normal. This function equips Huawei devices with a stronger adaptability to low-end devices.
BFD-capable
BFD-incapable
Forwarding to the source device according to DIP=A
SIP: source IP address
DIP: destination IP address
MD: my discriminator
YD: your discriminator
BFD SIP=A, DIP=A, MD=A, YD=A
BFD SIP=A, DIP=A, MD=A, YD=A
Router A
Router B
BFD
TI-LFA FRR
VPN FRR
Hot-Standby
Anycast FRR
Microloop Avoidance
SBFD

## Slide 83
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing

## Slide 84: Intra-AS SR-MPLS BE
SR-MPLS BE applies to services that do not have strict SLA requirements or require path planning.
Downstream routers allocate SIDs to upstream routers to form SR-MPLS forwarding paths.
MP-BGP is used on the control plane to advertise VPN labels.
SR-MPLS BE can be used as a backup solution for SR-MPLS TE services on a production network.
P1
P2
PE1
CE1
PE2
CE2
IGP (OSPF or IS-IS)
SR
MP-IBGP
MPLS
MPLS
MPLS
SID advertisement
SID advertisement
SID advertisement

## Slide 85: Intra-AS SR-MPLS TE
SR-MPLS TE applies to scenarios that have strict SLA requirements and require path planning, such as DCI scenarios.
SR labels are advertised by an IGP. The controller uses BGP-LS to collect information (e.g. network topology, bandwidth, latency, and label information).
The controller computes qualified forwarding paths based on constraints and delivers path computation results to forwarders through PCEP or NETCONF. Engineers can also manually configure strict forwarding paths and delegate the paths to the controller through PCEP.
Controller
BGP-LS, NETCONF, and PCEP
IDC 1
IDC 2
IGP

## Slide 86: Intra-AS SR-MPLS Policy
SR-MPLS Policy applies to scenarios that have strict SLA requirements and require path planning.
SR labels are advertised by an IGP. The controller uses BGP-LS to collect information (e.g. network topology, bandwidth, latency, and label information).
The controller computes qualified forwarding paths based on constraints and delivers path computation results to forwarders through BGP SR Policy or PCEP. Engineers can also manually configure strict forwarding paths and delegate the paths to the controller through PCEP.
Controller
BGP-LS, NETCONF,
and BGP SR Policy/PCEP
IGP
Notes: PCEP was first proposed in the optical transport field. It is seldom deployed on enterprises' production networks due to its few applications on IP networks, difficult interoperability between vendors, and poor performance. Therefore, BGP SR-Policy is recommended on an SR-MPLS network.

## Slide 87: Inter-AS E2E SR-MPLS TE (1)
In inter-AS access scenarios, it is recommended that the controller perform centralized computation and deliver E2E SR-MPLS TE paths.
BGP egress peer engineering (EPE) is configured on ASBRs for them to allocate a BGP peer SID to each other.
The ASBRs then use BGP-LS to report the BGP EPE-generated labels and network topology information.
AS 100
AS 200
Controller
ASBR
ASBR
PE1
PE2
BGP EPE
BGP peer SID reporting through BGP-LS
SID 304
SID 403

## Slide 88: Inter-AS E2E SR-MPLS TE (2)
Before an E2E SR-MPLS TE tunnel is created, the controller needs to create intra-AS SR-MPLS TE tunnels.
To reduce the label stack depth, you can configure a BSID for each intra-AS tunnel.
In this example, BSID 1000 is configured for the tunnel from PE1 to one ASBR, and BSID 2000 for the tunnel from PE2 to the other ASBR.
AS 100
AS 200
Controller
ASBR
ASBR
PE1
PE2
BSID 1000
BSID 2000
BGP EPE
SID 304
SID 403

## Slide 89: Inter-AS E2E SR-MPLS TE (3)
The controller performs global computation, integrates path labels into a label stack, and then delivers it to forwarders.
In this example, the label stack for the path from PE1 to PE2 is <1000, 304, 2000>.
In the label stack, 1000 and 2000 are BSIDs, which will be replaced with corresponding SR label stacks during intra-AS forwarding.
AS 100
AS 200
Controller
ASBR
ASBR
PE1
PE2
SID 304
SID 403
BSID 1000
BSID 2000

## Slide 90
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing
  SR-MPLS BE
  SR-MPLS TE
  SR-MPLS Policy

## Slide 91: L3VPN over SR-MPLS BE (1)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SR-MPLS BE tunnel on the backbone network so that CE1 and CE2 can communicate through Loopback1.
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 92: L3VPN over SR-MPLS BE (2)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
[~PE1] ospf 1
[*PE1-ospf-1] opaque-capability enable
[*PE1-ospf-1] quit
[~PE1] mpls lsr-id 10.0.1.1
[*PE1] mpls
[~PE1-mpls] quit
[~PE1] segment-routing
[*PE1-segment-routing] quit
[*PE1] ospf 1
[*PE1-ospf-1] segment-routing mpls
[*PE1-ospf-1] segment-routing global-block 16000 23999
[*PE1-ospf-1] quit
[*PE1] interface loopback 0
[*PE1-LoopBack1] ospf prefix-sid index 1
[*PE1-LoopBack1] quit
[*PE1] commit
PE1 configurations are as follows: (P and PE2 configurations are not provided.)
P: index 2
PE2: index 3
Configure the same SRGB.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Notes: Before configuring an SR-MPLS BE tunnel, you need to enable MPLS on each device in the SR-MPLS domain. The configuration procedure is as follows:
  Run the system-view command to enter the system view.
  Run the mpls lsr-id lsr-id command to configure an LSR ID for the local device.
    Note the following during LSR ID configuration:
      Configuring LSR IDs is the prerequisite for all MPLS configurations.
      LSRs do not have default LSR IDs, and such IDs must be manually configured.
      Using the address of a loopback interface as the LSR ID is recommended for an LSR.
  Run the mpls command to enable MPLS.
Basic SR-MPLS BE function configurations mainly involve enabling SR globally, specifying an SRGB, and configuring an SR prefix SID.
  Enable SR globally.
    Run the system-view command to enter the system view.
    Run the segment-routing command to enter the Segment Routing view.
    Run the commit command to commit the configuration.
    Run the quit command to return to the system view.

## Slide 93
Notes:   Specify an SRGB.
    Run the ospf process-id command to enter the OSPF view.
    Run the opaque-capability enable command to enable the opaque LSA capability.
    Run the segment-routing mpls command to enable SR for the corresponding OSPF topology.
    Run the segment-routing global-block begin-value end-value command to specify an OSPF SRGB.
    Run the commit command to commit the configuration.
    Run the quit command to return to the system view.
  Configure an SR prefix SID.
    Run the interface loopback loopback-number command to create a loopback interface and enter the interface view.
    Run the ospf enable [ process-id ] area area-id command to enable OSPF on the interface.
    Run the ip address ip-address { mask | mask-length } command to configure an IP address for the loopback interface.
    Run the ospf prefix-sid { absolute sid-value | index index-value } [ node-disable ] command to configure an SR prefix SID for the IP address of the interface.

## Slide 94: L3VPN over SR-MPLS BE (3)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
[~PE1] bgp 100
[~PE1-bgp] peer 10.0.3.3 as-number 100
[*PE1-bgp] peer 10.0.3.3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 10.0.3.3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1]bgp 100
[*PE1-bgp]ipv4-family vpn-instance vpna
[*PE1-bgp-vpna]peer 10.0.14.4 as-number 65000
PE1 configurations are as follows: (PE2 configurations are not provided.)
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 95: L3VPN over SR-MPLS BE (4)
[~PE1] tunnel-policy p1
[*PE1-tunnel-policy-p1] tunnel select-seq sr-lsp load-balance-number 2
[*PE1-tunnel-policy-p1] quit
[*PE1] commit
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] tnl-policy p1
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1] commit
<PE1>display tunnel-info all
Tunnel ID Type Destination Status
-------------------------------------------------------------------------------0x000000002900000042 srbe-lsp 10.0.3.3 UP
0x000000002900000043 srbe-lsp 10.0.2.2 UP
Run the display tunnel-info all command on PE1 to check SR LSP information.
PE1 configurations are as follows: (PE2 configurations are not provided.)
ID of the tunnel to PE2
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
Notes: Configure a tunnel policy and tunnel selection sequence.
  Run the system-view command to enter the system view.
  Run the tunnel-policy policy-name command to create a tunnel policy and enter the tunnel policy view.
  Run the tunnel select-seq sr-lsp load-balance-number load-balance-number [ unmix ] command to configure a tunnel selection sequence and the number of tunnels for load balancing.
  Run the commit command to commit the configuration.
  Run the quit command to return to the system view.
Configure BGP L3VPN service recursion to SR-MPLS BE tunnels.
  Run the ip vpn-instance vpn-instance-name command to enter the VPN instance view.
  Run the ipv4-family command to enter the VPN instance IPv4 address family view.
  Run the tnl-policy policy-name command to apply a tunnel policy to the VPN instance IPv4 address family.
  Run the commit command to commit the configuration.

## Slide 96: L3VPN over SR-MPLS BE (5)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
<PE1>display bgp vpnv4 all routing-table 10.1.5.5
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 10.1.5.5/32:
Label information (Received/Applied): 48122/NULL
From: 10.0.3.3 (10.0.3.3)
Route Duration: 0d00h39m18s
Relay IP Nexthop: 10.0.12.2
Relay IP Out-Interface: GigabitEthernet0/3/1
Relay Tunnel Out-Interface: GigabitEthernet0/3/1
Original nexthop: 10.0.3.3
Qos information : 0x0
Ext-Community: RT <111 : 1>
AS-path 65001, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 2
Not advertised to any peer yet
Check VPNv4 routing information on PE1.
Label allocated by PE2 to 10.1.5.5/32
Loopback0
10.0.3.3/32
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 97: L3VPN over SR-MPLS BE (6)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
<PE1>display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Route Flags: R - relay, D - download to fib, T - to vpn-instance
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 10.0.3.3 Neighbour: 10.0.3.3
State: Active Adv Relied Age: 00h35m03s
Tag: 0 Priority: low
Label: 48122 QoSInfo: 0x0
IndirectID: 0x100013A Instance:
RelayNextHop: 10.0.12.2 Interface: GigabitEthernet0/3/1
TunnelID: 0x000000002900000042 Flags: RD
Check vpna's routing information on PE1.
The VPNv4 label and SR LSP are combined to guide packet forwarding.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 98: L3VPN over SR-MPLS BE (7)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure a tunnel policy for the PEs to preferentially select SR LSPs.
Verify the configuration.
<PE1>tracert lsp segment-routing ip 10.0.3.3 32
LSP Trace Route FEC: SEGMENT ROUTING IPV4 PREFIX 10.0.3.3/32 , press CTRL_C to break.
TTL Replier Time Type Downstream
0 Ingress 10.0.12.2/[16003 ]
1 10.0.12.2 8 ms Transit 10.0.23.3/[3 ]
2 10.0.3.3 9 ms Egress
Tracert the SR LSP on PE1.
Question: How are the labels computed?
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 99
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing
  SR-MPLS BE
  SR-MPLS TE
  SR-MPLS Policy

## Slide 100: L3VPN over SR-MPLS TE (1)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SR-MPLS TE tunnel on the backbone network so that CE1 and CE2 can communicate through Loopback1.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 101: L3VPN over SR-MPLS TE (2)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
[~PE1] mpls lsr-id 10.0.1.1
[*PE1] mpls
[*PE1-mpls] mpls te
[*PE1-mpls] quit
[~PE1] segment-routing
[*PE1-segment-routing] quit
[~PE1] ospf 1
[*PE1-ospf-1] opaque-capability enable
[*PE1-ospf-1] segment-routing mpls
[*PE1-ospf-1] segment-routing global-block 16000 23999
[*PE1-ospf-1] area 0
[*PE1-ospf-1-area-0.0.0.0] mpls-te enable
[*PE1-ospf-1-area-0.0.0.0] quit
[*PE1] interface loopback 0
[*PE1-LoopBack1] ospf prefix-sid index 1
[*PE1-LoopBack1] quit
Configure basic SR-MPLS TE functions. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Notes: Before configuring an SR-MPLS TE tunnel, you need to enable MPLS TE on each device in the SR-MPLS domain.
  Run the system-view command to enter the system view.
    Run the mpls lsr-id lsr-id command to configure an LSR ID for the local device.
    Run the mpls command to enter the MPLS view.
    Run the mpls te command to enable MPLS TE globally on the local device.
  (Optional) Enable interface-specific MPLS TE. In a scenario where the controller or ingress performs path computation, interface-specific MPLS TE must be enabled. In a static explicit path scenario, this step can be ignored.
    Run the quit command to return to the system view.
    Run the interface interface-type interface-number command to enter the view of an interface on an MPLS TE link.
    Run the mpls command to enable MPLS on the interface.
    Run the mpls te command to enable MPLS TE on the interface.
  Run the commit command to commit the configuration.

## Slide 102
Notes: SR-MPLS TE supports both strict and loose explicit paths. Strict explicit paths mainly use adjacency SIDs, while loose explicit paths use both adjacency and node SIDs. Before configuring an SR-MPLS TE tunnel, perform the following steps to generate adjacency and node SIDs:
  Specify an SRGB.
    Run the system-view command to enter the system view.
    Run the ospf process-id command to enter the OSPF view.
    Run the opaque-capability enable command to enable the opaque LSA capability.
    Run the segment-routing mpls command to enable SR for the corresponding OSPF topology.
    Run the segment-routing global-block begin-value end-value command to specify an OSPF SRGB.
    Run the area area-id command to enter the OSPF area view.
    Run the mpls-te enable [ standard-complying ] command to enable TE in the current OSPF area.
  Configure an SR prefix SID.
    Run the interface loopback loopback-number command to create a loopback interface and enter the interface view.
    Run the ospf enable [ process-id ] area area-id command to enable OSPF on the interface.
    Run the ip address ip-address { mask | mask-length } command to configure an IP address for the loopback interface.
    Run the ospf prefix-sid { absolute sid-value | index index-value } [ node-disable ] command to configure an SR prefix SID for the IP address of the interface.
  (Optional) Configure an adjacency SID.
    Adjacency SIDs are dynamically generated after OSPF SR is enabled. To disable this, run the segment-routing auto-adj-sid disable command. Dynamically generated adjacency SIDs may change after a device restart. If an explicit path uses such an adjacency SID and the associated device is restarted, the adjacency SID needs to be reconfigured. You can also manually configure an adjacency SID to facilitate the use of an explicit path.
    Run the segment-routing command to enter the Segment Routing view.
    Run the ipv4 adjacency local-ip-addr local-ip-address remote-ip-addr remote-ip-address sid sid-value command to configure a static SR adjacency SID.

## Slide 103: L3VPN over SR-MPLS TE (3)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
[~PE1]explicit-path te1
[*PE1-explicit-path-te1]next sid label 16002 type prefix
[*PE1-explicit-path-te1]next sid label 16003 type prefix
[*PE1-explicit-path-te1]commit
Configure an SR-MPLS TE explicit path. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
[*PE1] interface tunnel1
[*PE1-Tunnel1] ip address unnumbered interface LoopBack1
[*PE1-Tunnel1] tunnel-protocol mpls te
[*PE1-Tunnel1] destination 10.0.3.3
[*PE1-Tunnel1] mpls te tunnel-id 1
[*PE1-Tunnel1] mpls te signal-protocol segment-routing
[*PE1-Tunnel1] mpls te path explicit-path te1
[*PE1-Tunnel1] commit
[~PE1-Tunnel1] quit
Configure an SR-MPLS TE tunnel interface. PE1 configurations are as follows: (PE2 configurations are not provided.)
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Notes: In this example, an explicit path is established by specifying prefix SIDs.
An explicit path is a vector path comprised of a series of nodes that are arranged in the configuration sequence. The path through which an SR-MPLS TE LSP passes can be planned by specifying next-hop labels or next-hop IP addresses on an explicit path. Generally, the IP addresses involved in an explicit path are interface IP addresses. An explicit path that is in use can be updated. To configure an explicit path, perform the following steps:
  Run the system-view command to enter the system view.
  Run the explicit-path path-name command to create an explicit path and enter the explicit path view.
  Run the next sid label label-value type { adjacency | prefix | binding-sid } command to specify a next-hop SID for the explicit path.
  Run the commit command to commit the configuration.

## Slide 104
Notes: SR-MPLS TE tunnels are established and managed using tunnel interfaces. As such, you need to configure a tunnel interface on the ingress of each SR-MPLS TE tunnel.
  Run the system-view command to enter the system view.
  Run the interface tunnel tunnel-number command to create a tunnel interface and enter the tunnel interface view.
  Configure an IP address for the tunnel interface.
    Run the ip address unnumbered interface interface-type interface-number command to specify an unnumbered IP address for the tunnel interface.
    An SR-MPLS TE tunnel is unidirectional and does not need a peer IP address. A separate IP address for the tunnel interface is not recommended. The LSR ID of the ingress is generally used as the tunnel interface's IP address.
  Run the tunnel-protocol mpls te command to configure MPLS TE as the tunneling protocol.
  Run the destination ip-address command to configure a destination address for the tunnel. Generally, the destination address of a tunnel is the LSR ID of the egress.
    Different types of tunnels have different requirements for the destination address. When the tunneling protocol is changed to MPLS TE from another type, the configured destination address is automatically deleted and needs to be reconfigured.
  Run the mpls te tunnel-id tunnel-id command to configure a tunnel ID.
  Run the mpls te signal-protocol segment-routing command to set the signaling protocol of the TE tunnel to SR.
  Run the mpls te path explicit-path path-name [ secondary ] command to specify an explicit path for the tunnel.
  The value of path-name must be the same as the name of the explicit path created using the explicit-path path-name command.

## Slide 105: L3VPN over SR-MPLS TE (4)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
[~PE1] bgp 100
[~PE1-bgp] peer 10.0.3.3 as-number 100
[*PE1-bgp] peer 10.0.3.3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 10.0.3.3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1]bgp 100
[*PE1-bgp]ipv4-family vpn-instance vpna
[*PE1-bgp-vpna]peer 10.0.14.4 as-number 65000
PE1 configurations are as follows: (PE2 configurations are not provided.)
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 106: L3VPN over SR-MPLS TE (5)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
[~PE1] tunnel-policy p2
[*PE1-tunnel-policy-p2] tunnel select-seq sr-te load-balance-number 1
[*PE1-tunnel-policy-p2] quit
[*PE1] commit
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] tnl-policy p2
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1] commit
Tunnel ID Type Destination Status
-----------------------------------------------------------------------------------
0x000000000300000001 sr-te 10.0.3.3 UP
0x000000002900000042 srbe-lsp 10.0.3.3 UP
0x000000002900000043 srbe-lsp 10.0.2.2 UP
Run the display tunnel-info all command on PE1 to check SR LSP information.
PE1 configurations are as follows: (PE2 configurations are not provided.)
ID of the SR-TE tunnel to PE2
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 107: L3VPN over SR-MPLS TE (6)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
[~PE1]display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Route Flags: R - relay, D - download to fib, T - to vpn-instance, B - black hole route
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 10.0.3.3 Neighbour: 10.0.3.3
State: Active Adv Relied Age: 00h04m18s
Tag: 0 Priority: low
Label: 48122 QoSInfo: 0x0
IndirectID: 0x100013D Instance:
RelayNextHop: 0.0.0.0 Interface: Tunnel1
TunnelID: 0x000000000300000001 Flags: RD
Check vpna's routing information on PE1.
The VPNv4 label and SR TE LSP are combined to guide packet forwarding.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 108: L3VPN over SR-MPLS TE (7)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS, configure SR, and establish SR-MPLS TE LSPs on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy for the PEs to preferentially select SR-MPLS TE LSPs.
Verify the configuration.
<PE1>tracert lsp segment-routing te Tunnel 1
LSP Trace Route FEC: SEGMENT ROUTING TE TUNNEL IPV4 SESSION QUERY Tunnel1 , press CTRL_C to break.
TTL Replier Time Type Downstream
0 Ingress 10.0.12.2/[16003 ]
1 10.0.12.2 21 ms Transit 10.0.23.3/[3 ]
2 10.0.3.3 9 ms Egress
Tracert the SR LSP on PE1.
Question: How are the labels computed?
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 109
Segment Routing Overview
Segment Routing Fundamentals
Segment Routing Tunnel Protection and Detection Technologies
Typical Usage Scenarios of Segment Routing
Basic Configurations of Segment Routing
  SR-MPLS BE
  SR-MPLS TE
  SR-MPLS Policy

## Slide 110: L3VPN over Static SR-MPLS Policy (1)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to static SR-MPLS Policy on the backbone network so that CE1 and CE2 can communicate through Loopback1.
PE1
P
PE2
10.0.12.0/24
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
10.0.23.0/24
VPN: vpna
Loopback1
10.1.5.5/32
.1
.2
.2
.3
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24

## Slide 111: L3VPN over Static SR-MPLS Policy (2)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
[~PE1] mpls lsr-id 10.0.1.1
[*PE1] mpls
[*PE1-mpls] mpls te
[*PE1-mpls] quit
[~PE1] segment-routing
[*PE1-segment-routing] ipv4 adjacency local-ip-addr 10.0.12.1 remote-
ip-addr 10.0.12.2 sid 330012
[*PE1-segment-routing] quit
[~PE1] ospf 1
[*PE1-ospf-1] opaque-capability enable
[*PE1-ospf-1] segment-routing mpls
[*PE1-ospf-1] segment-routing global-block 16000 23999
[*PE1-ospf-1-area-0.0.0.0] quit
[*PE1] interface loopback 0
[*PE1-LoopBack1] ospf prefix-sid index 1
[*PE1-LoopBack1] quit
Configure basic SR-MPLS functions. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
In scenarios where SR-MPLS Policies are statically configured, you are advised to use statically configured adjacency SIDs.
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032
Notes: In this example, adjacency SIDs are configured statically. The values of adjacency SIDs are shown in the figure.

## Slide 112: L3VPN over Static SR-MPLS Policy (3)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
[~PE1] segment-routing
[~PE1-segment-routing] segment-list pe1
[*PE1-segment-routing-segment-list-pe1] index 10 sid label 330012
[*PE1-segment-routing-segment-list-pe1] index 20 sid label 330023
[*PE1-segment-routing-segment-list-pe1] quit
[*PE1-segment-routing] sr-te policy policy100 endpoint 10.0.3.3 color 100
[*PE1-segment-routing-te-policy-policy100] binding-sid 115
[*PE1-segment-routing-te-policy-policy100] mtu 1000
[*PE1-segment-routing-te-policy-policy100] candidate-path preference 200
[*PE1-segment-routing-te-policy-policy100-path] segment-list pe1
[*PE1-segment-routing-te-policy-policy100-path] quit
[*PE1-segment-routing-te-policy-policy100] quit
[*PE1-segment-routing] quit
[*PE1] commit
Configure an SR-MPLS Policy. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
Configure a destination address and color for the SR-MPLS Policy.
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032
Notes: SR-MPLS Policies are used to direct traffic to traverse an SR-MPLS TE network. Each SR-MPLS Policy can have multiple candidate paths with different preferences. A valid candidate path with the highest preference is selected as the primary path, and a valid candidate path with the second highest preference as the backup path. The SR-MPLS Policy configuration procedure is as follows:
  Configure a segment list.
    Run the system-view command to enter the system view.
    Run the segment-routing command to enable SR globally and enter the Segment Routing view.
    Run the segment-list (Segment Routing view) list-name command to configure a segment list for an SR-MPLS TE candidate path and enter the segment list view.
    Run the index index sid label label command to specify a next-hop SID for the segment list.
      You can run the command multiple times. The system generates a label stack for the segment list by index in ascending order. If a candidate path in an SR-MPLS Policy is preferentially selected, traffic is forwarded using the segment list of the candidate path. A maximum of 10 SIDs can be configured for each segment list.

## Slide 113
Notes:   Configure an SR-MPLS Policy.
    Run the system-view command to enter the system view.
    Run the segment-routing command to enable SR globally and enter the Segment Routing view.
    Run the sr-te policy policy-name [ endpoint ipv4-address color color-value ] command to create an SR-MPLS Policy with the specified endpoint and color and enter the SR-MPLS Policy view.
    (Optional) Run the binding-sid label-value command to configure a binding SID for the SR-MPLS Policy.
    The value of label-value must be within the range defined using the local-block begin-value end-value command.
    (Optional) Run the mtu mtu command to configure an MTU for the SR-MPLS Policy.
    Run the candidate-path preference preference command to configure a candidate path and its preference for the SR-MPLS Policy.
    Each SR-MPLS Policy supports multiple candidate paths. A larger preference value indicates a higher candidate path preference. If multiple candidate paths are configured, the one with the highest preference takes effect.
    Run the segment-list (candidate path view) list-name command to reference the specified segment list of the corresponding SR-MPLS TE candidate path.
    The segment list must have been created using the segment-list (Segment Routing view) command.

## Slide 114: L3VPN over Static SR-MPLS Policy (4)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1] interface loopback1
[*PE1-LoopBack1] ip binding vpn-instance vpna
[*PE1-LoopBack1] ip address 10.1.4.4 24
[*PE1-LoopBack1] quit
[~PE1] route-policy color100 permit node 1
[*PE1-route-policy] apply extcommunity color 0:100
[~PE1] bgp 100
[~PE1-bgp] peer 10.0.3.3 as-number 100
[*PE1-bgp] peer 10.0.3.3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 10.0.3.3 enable
[*PE1-bgp-af-vpnv4] peer 10.0.3.3 route-policy color100 import
[~PE1-bgp-af-vpnv4] quit
[*PE1-bgp]ipv4-family vpn-instance vpna
[*PE1-bgp-vpna]import-route direct
[*PE1-bgp-vpna]commit
PE1 configurations are as follows: (PE2 configurations are not provided.)
Add the color attribute to the received route.
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032
Notes: The color attribute is added to a route through a route-policy. This enables the route to recurse to an SR-MPLS Policy based on the color value and next-hop address in the route.
  Configure a route-policy.
    Run the system-view command to enter the system view.
    Run the route-policy route-policy-name { deny | permit } node node command to create a route-policy and enter the route-policy view.
    (Optional) Configure if-match clauses for the route-policy. The community attributes of routes can be added or modified only if the routes match specified if-match clauses.
    Run the apply extcommunity color color command to configure a BGP extended community, that is, the color attribute.
    Run the commit command to commit the configuration.

## Slide 115
Notes:   Apply the route-policy to the specified BGP VPNv4 peer.
    Run the system-view command to enter the system view.
    Run the bgp as-number command to enter the BGP view.
    Run the peer { ipv4-address | group-name } as-number { as-number-plain | as-number-dot } command to create a BGP peer.
    Run the ipv4-family vpnv4 command to enter the BGP VPNv4 address family view.
    Run the peer { ipv4-address | group-name } enable command to enable the BGP VPNv4 peer relationship.
    Run the peer { ipv4-address | group-name } route-policy route-policy-name { import | export } command to configure a BGP import or export route-policy.
    Run the commit command to commit the configuration.

## Slide 116: L3VPN over Static SR-MPLS Policy (5)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
[~PE1] tunnel-policy p3
[*PE1-tunnel-policy-p3] tunnel select-seq sr-te-policy load-balance-
number 1 unmix
[*PE1-tunnel-policy-p3] quit
[*PE1] commit
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] tnl-policy p3
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1] commit
<PE1>display tunnel-info all
Tunnel ID Type Destination Status
-------------------------------------------------------------------------------
0x000000000300000001 sr-te 10.0.3.3 UP
0x000000002900000042 srbe-lsp 10.0.3.3 UP
0x000000002900000043 srbe-lsp 10.0.2.2 UP
0x000000003200000001 srtepolicy 10.0.3.3 UP
Run the display tunnel-info all command on PE1 to check SR LSP information.
PE1 configurations are as follows: (PE2 configurations are not provided.)
Tunnel ID of the SR-TE Policy destined for PE2
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032

## Slide 117: L3VPN over Static SR-MPLS Policy (6)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
[~PE1]display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Route Flags: R - relay, D - download to fib, T - to vpn-instance, B - black hole route
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 10.0.3.3 Neighbour: 10.0.3.3
State: Active Adv Relied Age: 00h01m04s
Tag: 0 Priority: low
Label: 48122 QoSInfo: 0x0
IndirectID: 0x100013F Instance:
RelayNextHop: 0.0.0.0 Interface: policy100
TunnelID: 0x000000003200000001 Flags: RD
Check vpna's routing information on PE1.
The VPNv4 label and SR-TE Policy LSP are combined to guide packet forwarding.
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032

## Slide 118: L3VPN over Static SR-MPLS Policy (7)
Configuration roadmap:
Configure interface IP addresses and OSPF. (Configuration details are not provided.)
Enable MPLS and configure an SR-MPLS Policy on the backbone network.
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable the VPN instance IPv4 address family on each PE.
Configure the color attribute for routes on the PEs and enable the PEs to exchange routing information.
Configure a tunnel policy on the PEs.
Verify the configuration.
<PE1>tracert lsp sr-te policy endpoint-ip 10.0.3.3 color 100
sr-te policy's segment list:
Preference: 200; Path Type: primary; Protocol-Origin: local; Originator: 0, 0.0.0.0; Discriminator: 200; Segment-List ID: 65; Xcindex: 2000065
TTL Replier Time Type Downstream
0 Ingress 10.0.12.2/[330023 ]
1 10.0.12.2 24 ms Transit 10.0.23.3/[3 ]
2 10.0.3.3 113 ms Egress
Tracert the SR LSP on PE1.
Question: How are the labels computed?
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
PE1
P
PE2
Loopback0
10.0.1.1/32
Loopback0
10.0.2.2/32
Loopback0
10.0.3.3/32
VPN: vpna
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
VPN: vpna
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
330012
330021
330023
330032

## Slide 119
(Single-answer question) Which of the following types of LSAs is used by OSPF to carry node IDs? ( )
  Type 1
  Type 2
  Type 7
  Type 10
Notes: D

## Slide 120
(Multiple-answer question) Which of the following ports are used by SBFD packets by default? ( )
  4784
  3784
  6784
  7784
Notes: AD

## Slide 121
SR is designed to forward data packets on a network using the source routing model. Compared with LDP and RSVP-TE, SR-MPLS simplifies the control plane of an MPLS network, enabling information such as labels to be carried only through IGP extensions. It provides higher scalability, freeing transit nodes from maintaining path information. The packet forwarding path can be controlled only by using the ingress. In addition, SR-MPLS can work with the centralized path computation module to flexibly and easily control and adjust paths, achieving smoother evolution to SDN.
SR-MPLS supports three types of LSPs: SR-MPLS BE, SR-MPLS TE, and SR-MPLS Policy. SR-MPLS provides multiple detection and protection mechanisms for these different LSPs, such as TI-LFA FRR, anycast FRR, hot standby, VPN FRR, microloop avoidance, BFD, and SBFD.
SR-MPLS supports both traditional and SDN networks, is compatible with existing devices, and supports multiple scenarios such as inter-AS interconnection. To facilitate understanding, this course provides examples for configuring SR-MPLS using commands. In the following courses, we will introduce how to use the controller to configure SR-MPLS.