## Slide 1
Datacom
General
V1.0
Wan Changli/WX408647
2021.2.22
Liu Shuying/00245623, Wang Qiusheng/00287740
New
He Junjian/WX580230
2021.4.13
Zhu Shigeng/00261992, Wan Changli/WX408647
Update
Wu Yue/wwx291773
2021.9.16
Lu Yueyue/WX445705
Update

## Slide 2: SRv6 Fundamentals and Configuration

## Slide 3
At the beginning of the Segment Routing (SR) architecture design, two implementation modes were designed for the data plane. One is Segment Routing-Multiprotocol Label Switching (SR-MPLS), which reuses the MPLS data plane and can be incrementally deployed on the existing IP/MPLS network. The other is Segment Routing IPv6 (SRv6), which uses the IPv6 data plane and implements extension based on the IPv6 Routing header.
This document describes the concepts and fundamentals of SRv6 and its applications for Huawei NetEngine series routers.

## Slide 4
On completion of this course, you will be able to:
  Describe the background of SRv6.
  Describe the technical advantages of SRv6.
  Describe the basic concepts and fundamentals of SRv6.
  Describe the concepts and fundamentals of SRv6 high reliability.
  Describe how to configure SRv6 BE and static SRv6 Policies.
  Describe how to deploy SRv6 using iMaster NCE-IP.

## Slide 5
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 6: IP/MPLS Network Introduction
As a Layer 2.5 technology that runs between Layer 2 and Layer 3, MPLS adds connection-oriented attributes to connectionless IP networks. Traditional MPLS label-based forwarding improves the forwarding efficiency of IP networks. However, as hardware capabilities continue to improve, MPLS no longer features distinct advantages in forwarding efficiency. Nevertheless, MPLS provides good QoS guarantee for IP networks through connection-oriented label forwarding and also supports TE, VPN, and FRR.
IP/MPLS networks have gradually replaced dedicated networks, such as ATM, frame relay (FR), and X.25. Ultimately, MPLS is applied to various networks, including IP backbone, metro, and mobile transport, to support multi-service transport and implement the Internet's all-IP transformation.
IP header-based forwarding
MPLS label-based forwarding
MPLS label-based forwarding
IP header-based forwarding
IP network
IP network
10.1.1.0/24
IP
Packet
MPLS
Header
Ethernet
Header
Destination: 10.1.1.1
IP/MPLS network
Notes: In the initial stage of network development, multiple types of networks, such as X.25, FR, ATM, and IP, co-existed to meet different service requirements. These networks could not interwork with each other, and on top of that, also competed, with mainly ATM and IP networks taking center stage. ATM is a transmission mode that uses fixed-length cell switching. It establishes paths in connection-oriented mode, and can provide better QoS capabilities than IP. The design philosophy of ATM involves centering on networks and providing reliable transmission, and its design concepts reflect the reliability and manageability requirements of telecommunications networks. This is the reason why ATM was widely deployed on early telecommunications networks. The design concepts of IP differ greatly from those of ATM. To be more precise, IP is a connectionless communication mechanism that provides the best-effort forwarding capability, and the packet length is not fixed. On top of that, IP networks mainly rely on the transport-layer protocols (e.g., TCP) to ensure transmission reliability, and the requirement for the network layer involves ease of use. The design concept of IP networks embodies the "terminal-centric and best-effort" notion of the computer network, enabling IP to meet the computer network's service requirements. The competition between the two can essentially be represented as a competition between telecommunications and computer networks. As the network scale expanded and network services increased in number, ATM networks became more complex than IP networks, while also bearing higher management costs. Within the context of costs versus benefits for telecom carriers, ATM networks were gradually replaced by IP networks.

## Slide 7
Notes: Although IP is more suitable for the development of computer networks than ATM, computer networks require a certain level of QoS guarantee. To compensate for the IP network's insufficient QoS capabilities, numerous technologies integrating IP and ATM, such as local area network emulation (LANE) and IP over ATM (IPoA), have been proposed. However, these technologies only addressed part of the issue, until 1996 when MPLS technology was proposed to provide a better solution to this issue.

## Slide 8: Issues with MPLS LDP and RSVP-TE
MPLS LDP
RSVP-TE
R1
R2
R4
R3
IGP
LDP itself does not have the path computation capability and requires an IGP for path computation.
Both the IGP and LDP need to be deployed for the control plane, and devices need to exchange a large number of packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
If LDP-IGP synchronization is not achieved, data forwarding may fail.
RSVP-TE configuration is complex and load balancing is not supported.
To implement TE, devices need to exchange a large number of RSVP packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
RSVP-TE uses a distributed architecture, so that each device only knows its own state and needs to exchange signaling packets with other devices.
LDP
LDP
LDP
LDP
IGP
IGP
IGP
R1
R2
R4
R3
RSVP response
RSVP response
RSVP request
RSVP request

## Slide 9: SR Origin and Solution
The SDN concept has a great impact on the network industry, and many protocols used for SDN implementation emerge in the industry, including OpenFlow, Protocol Oblivious Forwarding (POF), Programming Protocol-independent Packet Processors (P4), and SR. Compared with revolutionary protocols, SR considers compatibility with the existing network and smooth evolution, and also provides programmability. It is a de facto SDN standard.
  Advantages
  Disadvantages
SRv6
Extension based on the IPv6 Routing header
SR-MPLS
Incremental deployment on the existing IP/MPLS network
  Solutions
IP
LDP
RSVP-TE
ECMP
Label-based forwarding
Bandwidth reservation
Path planning
Lack of the path planning capability
Complex configuration/maintenance
Lack of the load balancing capability
No support for large-scale deployment
LDP-IGP synchronization issue
Simple configuration
Notes: SR resolves many issues on IP/MPLS networks through two solutions: SR-MPLS (based on MPLS forwarding) and SRv6 (based on IPv6 forwarding).

## Slide 10: From MPLS to SRv6
MPLS causes isolated network islands. SRv6 provides a unified forwarding plane and has advantages such as simplified protocols, high scalability, and programmability.
Forwarding plane
Control plane
Classic MPLS
SR-MPLS
LDP
RSVP-TE
IGP
IGP + SR extension
Payload
Payload
Push
Swap
Pop
Payload
Payload
Push
Continue
Next
SRv6
IGP + SR extension
Payload
Payload
IPv6 + SRH
Payload
Payload
IPv6 + SRH
Payload
MPLS 222
MPLS 111
Payload
MPLS 111
Payload
MPLS 1949
MPLS 2004
Payload
MPLS 1949
MPLS 1368
Control plane simplification
Forwarding plane simplification
Simplified protocols
High scalability
Programmability
Notes: Although MPLS plays an important role in the all-IP transformation of networks, it causes isolated network islands. On the one hand, it increases the complexity of cross-domain network interconnection. For example, solutions such as the MPLS VPN Option A/B/C solution are complex to deploy and involve difficult E2E service deployment. On the other hand, as the Internet and cloud computing develop, more and more cloud data centers are built. To meet tenants' networking requirements, multiple overlay technologies have been proposed, among which VXLAN is a typical example. In the past, quite a few attempts were made to provide VPN services by introducing MPLS to data centers. However, these attempts all wound up in failure due to multiple factors, including numerous network boundaries, complex management, and insufficient scalability. As such, the traffic from an end user to a service in a data center may typically need to pass through the VLAN, IP network, IP/MPLS network, and VXLAN network.
The combination of MPLS and SR is intended to provide programmability for networks as a practice of SDN implementation. However, this cannot satisfy services (such as SFC and IOAM) that need to carry metadata, as MPLS encapsulation has poor scalability. Nowadays, the IPv4 address space is almost exhausted. IPv6 and SR are combined, promoting the advent of SRv6.

## Slide 11: Technical Benefits of SRv6
SRv6 simplifies existing network protocols and network management. In addition, SRv6 supports native IPv6 and provides the network programming capability, making SRv6 more advantageous.
  Thanks to the native IPv6 attribute, SRv6 can better promote cloud-network convergence, be compatible with existing networks, and improve inter-AS experience.
  Thanks to the network programming capability, SRv6 can not only better implement path programming to meet service SLAs but also connect networks and applications to build intelligent cloud-networks.
AS 65000
AS 65001
High-bandwidth path
Low-delay path
Controller
Ingress
Data download
Video
Compatibility with existing networks
Path programming to meet service SLAs
Common IPv6 router
SRv6 router
Promotion of cloud-network convergence
Improved inter-AS experience

## Slide 12
SRv6 Overview
SRv6 Fundamentals
  Basic Concepts of SRv6
  SRv6 Policy Path Establishment and Traffic Steering
  Typical SRv6 Applications
SRv6 High Reliability
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 13: SRv6 Fundamentals
SRv6 adds a Segment Routing header (SRH) to data on the ingress to guide data forwarding.
Without changing the original encapsulation format of IPv6 packets, SRv6 packets are still IPv6 ones and can be identified by common IPv6 devices. As such, SRv6 is a native IPv6 technology.
SRv6's native IPv6 attribute enables SRv6 devices to interwork with common IPv6 devices, offering excellent compatibility on an existing network.
Ingress
IPv6 Header
D C B
Payload
B
C
D
IPv6 Header
D C B
Payload
IPv6 Header
D C B
Payload
SRH
IPv6 Header
Payload

## Slide 14: IPv6 SRH
RFC 8754 defines the IPv6 SRH added to IPv6 packets. The SRH format is as follows:
The value 43 indicates a routing extension header.
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type=4 |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List [0] (128-bit IPv6 address) |  |  |  | 
Segment List [1] (128-bit IPv6 address) |  |  |  | 
Segment List [2] (128-bit IPv6 address) |  |  |  | 
Optional TLV objects (variable) |  |  |  | 
IPv6 Payload |  |  |  | 
An SRH contains the following fields:
  Segment List: an ordered list of SRv6 segment identifiers (SIDs).
  Segments Left (SL): number of remaining SRv6 segments. The SL value is decremented and the destination IP address (DIP) is changed to an active SID to complete traffic forwarding segment by segment.
  Tag: tags a packet as part of a class or group of packets to implement group-based policies.
  SRH TLVs (e.g. NSH metadata, HMAC TLV, and Padding TLV): can be used as global parameters of SIDs in segment lists.
The recommended value of Routing Type for a routing extension header is 4, indicating an SR header (called SR extension header or SRH).
Active segment
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: The biggest difference between SRv6 and SR-MPLS lies in the IPv6 SRH. SRv6 uses IPv6 extension headers to implement Segment Routing.
For details, see https://datatracker.ietf.org/doc/rfc8754.

## Slide 15: SRv6 Segment
SRv6 segments are expressed using IPv6 addresses and usually called SRv6 SIDs.
As shown in the figure, an SRv6 SID usually consists of three fields: Locator, Function, and Arguments. They are expressed in the Locator:Function:Arguments format. Note that the total length (Locator + Function + Arguments) is less than or equal to 128 bits. If the total length is less than 128 bits, the reserved bits are padded with 0.
If the Arguments field does not exist, the format is Locator:Function. The Locator field occupies the most significant bits of an IPv6 address, and the Function field occupies the remaining part of the IPv6 address.
SRv6 segment: IPv6 address format
IPv6 Header | IPv6 SRH (IPv6 Extension Header) |  |  | IPv6 Payload
 | 128 bits | 128 bits | 128 bits | 
Locator | Function | Arguments
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 16: SRv6 Segment: Locator
The Locator field identifies the location of a network node, and is used for other nodes to route and forward packets to this identified node so as to implement network instruction addressing.
A locator has two important characteristics: routable and aggregatable. After a locator is configured for a node, the system generates a locator route and propagates the route throughout the SR domain using an IGP, allowing other nodes to locate the node based on the received locator route information. In addition, all SRv6 SIDs advertised by the node are reachable through the route.
In the following example, a locator with the 64-bit prefix 2001:DB8:ABCD:: is configured for a Huawei device.
128 bits
IPv6 prefix
[Huawei] segment-routing ipv6
[Huawei-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64
Locator | Function | Arguments
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: The locator is routable and therefore usually unique in an SR domain. In some scenarios, such as an anycast protection scenario, multiple devices may be configured with the same locator.

## Slide 17: SRv6 Segment: Function & Arguments
The Function field identifies the forwarding behavior to be performed. In SRv6 network programming, forwarding behaviors are identified using different functions. For example, RFC defines End, End.X, End.DX4, and End.DX6 behaviors.
An End.X SID is similar to an adjacency SID in SR-MPLS and is used to identify a link. A configuration example is as follows:
128 bits
Opcode
Optional
[Huawei-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64
[Huawei-segment-routing-ipv6] opcode ::1 end-x interface G3/0/0 next-hop 2001:DB8:200::1
The opcode corresponding to the function is ::1. In this example, the Arguments field is not carried, and the SRv6 SID is 2001:db8:abcd::1.
This function guides packet forwarding from the specified interface (G3/0/0) to the corresponding neighbor (2001:DB8:200::1).
Locator | Function | Arguments
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: In some scenarios, an SRv6 endpoint behavior may require additional actions. In this case, the Arguments field must be encapsulated. For example, in an EVPN VPLS scenario where CE multi-homing is deployed for BUM traffic forwarding, the Function field is set to End.DT2M, and the Arguments field is used to provide local ESI mapping to implement split horizon.
The Function and Arguments fields can both be defined by engineers, resulting in an SRv6 SID structure that improves network programmability. In most scenarios, the Arguments field is not configured.

## Slide 18: SRv6 Segment Types
Category | Function Description | Protocol | Type
End | Indicates an endpoint SID that identifies a destination node. The corresponding function is to update the IPv6 DA and then search the IPv6 forwarding information base (FIB) for packet forwarding. | IGP | Path SID
End.X | Indicates a Layer 3 cross-connect endpoint SID that identifies a link. The corresponding function is to update the IPv6 DA and then forward packets through the outbound interface bound to the End.X SID. | IGP | Path SID
End.DT4 | Indicates a PE-specific endpoint SID that identifies an IPv4 VPN instance. The corresponding function is to decapsulate packets and then search the routing table of the involved IPv4 VPN instance for packet forwarding. This SID is equivalent to an IPv4 VPN label and used in L3VPNv4 scenarios. | BGP | Service SID
End.DT6 | Indicates a PE-specific endpoint SID that identifies an IPv6 VPN instance. The corresponding function is to decapsulate packets and then search the routing table of the involved IPv6 VPN instance for packet forwarding. This SID is equivalent to an IPv6 VPN label and used in L3VPNv6 scenarios. | BGP | Service SID
End.DX4 | Indicates a PE-specific Layer 3 cross-connect endpoint SID that identifies an IPv4 CE. The corresponding function is to decapsulate packets and then forward the resulting IPv4 packets through the Layer 3 interface bound to the SID. This SID is equivalent to a label identifying an adjacency to a CE and used in L3VPNv4 scenarios. | BGP | Service SID
End.DX6 | Indicates a PE-specific Layer 3 cross-connect endpoint SID that identifies an IPv6 CE. The corresponding function is to decapsulate packets and then forward the resulting IPv6 packets through the Layer 3 interface bound to the SID. This SID is equivalent to a label identifying an adjacency to a CE and used in L3VPNv6 scenarios. | BGP | Service SID
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: In addition to L3VPN services, SRv6 can carry L2VPN services. L2VPN-related SIDs are as follows:
  End.DX2: Indicates a Layer 2 cross-connect endpoint SID that identifies an endpoint. The corresponding function is to decapsulate packets, remove the IPv6 header (along with all its extension headers), and then forward the remaining packet data to the outbound interface associated with the SID. This SID can be used in EVPN VPWS scenarios. If a bypass tunnel exists on the network, an End.DX2L SID is generated automatically.
  End.DT2U: Indicates a Layer 2 cross-connect endpoint SID that requires unicast MAC table lookup and identifies an endpoint. If a bypass tunnel exists on the network, an End.DT2UL SID is generated automatically. This SID can be used to guide unicast traffic forwarding over the bypass tunnel when a CE is dual-homed to PEs. The corresponding function is to remove the IPv6 header (along with all its extension headers), search the MAC address table for a MAC entry based on the exposed destination MAC address, and then forward the remaining packet data to the corresponding outbound interface based on the entry. This SID can be used in EVPN VPLS unicast scenarios.

## Slide 19
Notes:   End.DT2M: Indicates a Layer 2 cross-connect endpoint SID that requires broadcast-based flooding and identifies an endpoint. The corresponding function is to remove the IPv6 header (along with all its extension headers) and then broadcast the remaining packet data in the Bridge Domain (BD). This SID can be used in EVPN VPLS BUM scenarios.
SRv6 SID mainly used for SRv6 O&M:
  End.OP (OAM Endpoint with Punt): Indicates an OAM SID. The corresponding function is to send OAM packets to the OAM process. This SID is mainly used in ping/tracert scenarios.

## Slide 20: Naming Rules for SRv6 Segments
SRv6 segments are named according to certain rules. You can quickly determine the corresponding instruction function based on the naming rule combination.
  End: the most basic instruction executed by a segment endpoint node, directing the node to terminate the current instruction and start the next instruction. The corresponding forwarding behavior is to decrement the SL field by 1 and copy the SID pointed by the SL field to the DA field in the IPv6 header.
  X: forwards packets through one or a group of Layer 3 outbound interfaces.
  T: searches a specified routing table and forwards packets.
  D: decapsulates packets by removing the IPv6 header and related extension headers.
  V: searches a specified table for packet forwarding based on virtual local area network (VLAN) information.
  U: searches a specified table for packet forwarding based on unicast MAC address information.
  M: searches a Layer 2 forwarding table for multicast forwarding.
  B6: applies a specified SRv6 Policy.
  BM: applies a specified SR-MPLS Policy.
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 21: SRv6 Segment Examples
An End SID identifies a destination node. It is similar to a node SID in SR-MPLS. After an End SID is generated on a node, the node propagates the SID to all the other nodes in the SRv6 domain through an IGP. All nodes in the SRv6 domain know how to implement the instruction bound to the SID.
An End.X SID is a Layer 3 cross-connect endpoint SID that identifies a link. It is similar to an adjacency SID in SR-MPLS. After an End.X SID is generated on a node, the node propagates the SID to all the other nodes in the SRv6 domain through an IGP. Although the other nodes can all obtain the SID, only the node generating the SID knows how to implement the instruction bound to the SID.
An End.DT4 SID is a PE-specific endpoint SID that identifies an IPv4 VPN instance. The instruction bound to the End.DT4 SID is to decapsulate packets and search the routing table of the corresponding IPv4 VPN instance for packet forwarding. The End.DT4 SID is equivalent to an IPv4 VPN label and used in L3VPNv4 scenarios. It can be either manually configured or automatically allocated by BGP within the dynamic SID range of the specified locator.
PE1
P
PE2
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
AS 65001
AS 65002
End SID
2001:DB8:1000::111
End SID
2001:DB8:2000::222
End SID
2001:DB8:3000::333
End.X SID
2001:DB8:1000::12
End.X SID
2001:DB8:2000::21
End.X SID
2001:DB8:2000::23
End.X SID
2001:DB8:3000::32
VPNA: End.DT4 SID
2001:DB8:1000::1:0:1E
VPNA: End.DT4 SID
2001:DB8:3000::1:0:1E
AS 65000
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 22: SRv6 Flavors
Flavors are additional behaviors defined for SRv6 segment enhancement. These behaviors are optional and used to enhance SRv6 segment-based actions in order to meet diverse service requirements.
SRv6-Network-Programming defines the following additional behaviors: penultimate segment pop of the SRH (PSP), ultimate segment pop of the SRH (USP), and ultimate segment decapsulation (USD).
Flavor | Function Description | Attached End Instruction
PSP | Removes the SRH on the penultimate endpoint node. | End, End.X, End.DT2, End.DT4, and End.DT6
USP | Removes the SRH on the ultimate endpoint node. | End, End.X, End.DT2, End.DT4, and End.DT6
USD | Decapsulates the outer IPv6 header on the ultimate endpoint node. | End, End.X, End.DT2, End.DT4, and End.DT6
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: Different flavors can be combined. For example, if an End SID carries PSP and USP flavors, the PSP action is performed on the penultimate node, and the USD action is performed on the ultimate node.

## Slide 23: SRv6 Locator Configuration Commands
[Huawei] segment-routing ipv6
Enable SRv6 and enter the SRv6 view.
After running the segment-routing ipv6 command, you can configure a locator and SRv6 SID in the SRv6 view so that an SRv6 local SID forwarding entry can be generated.
[Huawei-segment-routing-ipv6] locator locator-name [ ipv6-prefix ipv6-address prefix-length [ [ static static-length ] | [ args args-length ] ] * ]
Configure an SRv6 SID locator.
An SRv6 SID is a 128-bit IPv6 address expressed in the Locator:Function:Arguments format.
The Locator field corresponds to the ipv6-prefix ipv6-address parameter and its length is determined by the prefix-length parameter.
The Function field is also called opcode, which can be dynamically allocated using an IGP or be configured using the opcode command. When configuring a locator, you can use the static static-length parameter to specify the static segment length, which determines the number of static opcodes that can be configured in the locator. In dynamic opcode allocation, the IGP allocates opcodes outside the range of the static segment, so that no SRv6 SID conflict occurs.
The Args field is determined by the args args-length parameter. It is optional in SRv6 SIDs and depends on command configurations.
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: static static-length: specifies the static segment length in the Function field. This length determines the number of static opcodes that can be configured in the specified locator.
args args-length: specifies the length of the Arguments field. The Arguments field is located at the end of a SID. If args args-length is configured, the Arguments field is reserved and will not be occupied by configured static SIDs or generated dynamic SIDs.

## Slide 24: SRv6 SID Configuration Commands
[Huawei-segment-routing-ipv6-locator] opcode func-opcode end [no-flavor | psp | psp-usp-usd ]
Configure a static End SID opcode.
An End SID identifies an SRv6 node.
[Huawei-segment-routing-ipv6-locator] opcode func-opcode end-x interface {interface-name | interface-type interface-number} nexthop nexthop-address [no-flavor | psp | psp-usp-usd]
Configure a static End.X SID opcode.
An End.X SID identifies a Layer 3 adjacency of an SRv6 node. Therefore, you need to specify an interface and the next hop address of the interface during the configuration.
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 25: SRv6 Locator Configuration Example
SRv6 SIDs can be statically configured or dynamically allocated. In dynamic allocation mode, only the locator command needs to be run, and the required opcode is dynamically allocated by an IGP. In static configuration mode, you need to manually configure an opcode for the SIDs of the corresponding type.
The relationship of parameters in the locator command is as follows:
In static configuration mode, SIDs occupy only the static segment with values starting from 1, and the dynamic segment is set to 0. In dynamic allocation mode, SIDs occupy both the dynamic segment and static segment. The values in the dynamic segment start from 1, and those in the static segment start from 0.
In this example, the locator 2001:DB8:ABCD:: is configured, and its length is 64 bits. The static segment occupies 32 bits, the dynamic segment 32 bits, and the Args field 0 bits. The value range is as follows:
  Static segment: The start value is 2001:DB8:ABCD:0000:0000:0000:0000:0001, and the end value is 2001:DB8:ABCD:0000:0000:0000:FFFF:FFFF.
  Dynamic segment: The start value is 2001:DB8:ABCD:0000:0000:0001:0000:0000, and the end value is 2001:DB8:ABCD:0000:FFFF:FFFF:FFFF:FFFF.
|--Locator--|--Dynamic Opcode--|--Static Opcode--|--Args--|
[Huawei-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64 static 32
Statically configuring End and End.X SIDs is recommended. Dynamically allocated SIDs will change after a device restart, adversely affecting maintenance.
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 26: SRv6 Node
RFC 8754 defines three types of SR nodes:
  SR source node: a source node that encapsulates packets with SRv6 headers.
  Transit node: an IPv6 node that forwards SRv6 packets but does not perform SRv6 processing.
  SRv6 segment endpoint node: a node that receives and processes SRv6 packets in which the destination IPv6 address is a local SID or local interface address of the node.
R1
FC01:: /96
Source Node
CE1
R2
Transit Node
R3
Endpoint Node
FC03:: /96
FC04:: /96
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
FC01::1
FC03::3
FC04::4
FC01:: /96
FC01::1
Locator
End SID
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 27: SRv6 Source Node
An SRv6 source node steers a packet using an SRv6 segment list. If the SRv6 segment list contains only one SID, and no Type Length Value (TLV) or other information needs to be added to the packet, the DA field of the packet is set to this SID.
An SRv6 source node can be either an SRv6-capable host where IPv6 packets originate or an edge device in an SRv6 domain.
IPv6 Header |  | 
SRH (SL = 2) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 
SRv6 Policy
R1
FC01:: /96
Source Node
CE1
R2
Transit Node
R3
Endpoint Node
FC03:: /96
FC04:: /96
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
FC01::1
FC03::3
FC04::4
FC01:: /96
FC01::1
Locator
End SID
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 28: Source Node Behaviors
An SRv6 source node steers packets into an SRv6 Policy and, if possible, encapsulates SRHs into the packets. The following table lists the behaviors of an SRv6 source node.
Source Node Behavior | Function Description
H.Insert | Inserts an SRH into a received IPv6 packet and searches the corresponding routing table for packet forwarding.
H.Insert.Red | Inserts a reduced SRH into a received IPv6 packet and searches the corresponding routing table for packet forwarding.
H.Encaps | Encapsulates an outer IPv6 header and SRH for a received IP packet, and searches the corresponding routing table for packet forwarding.
H.Encaps.Red | Encapsulates an outer IPv6 header and reduced SRH for a received IP packet, and searches the corresponding routing table for packet forwarding.
H.Encaps.L2 | Encapsulates an outer IPv6 header and SRH for a received Layer 2 frame, and searches the corresponding routing table for forwarding.
H.Encaps.L2.Red | Encapsulates an outer IPv6 header and reduced SRH for a received Layer 2 frame, and searches the corresponding routing table for forwarding.
IPv6 Header
SRH
Payload
IPv6 Header
Payload
Insert
IPv6 Header
SRH
IPv6 Header
Payload
IPv6 Header
Payload
Encaps
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: The difference between a reduced SRH and an SRH is that the segment list in a reduced SRH does not contain the first segment in an existing IPv6 DA.

## Slide 29: Transit Node
A transit node is an IPv6 node that does not participate in SRv6 processing on the SRv6 packet forwarding path. That is, the transit node just performs ordinary IPv6 packet forwarding.
After receiving an SRv6 packet, the node parses the IPv6 DA field in the packet. If the IPv6 DA is neither a locally configured SRv6 SID nor a local interface address, the node considers the SRv6 packet as an ordinary IPv6 packet and searches the routing table for packet forwarding without processing the SRH.
A transit node can be either an ordinary IPv6 node or an SRv6-capable node.
IPv6 Header |  | 
SRH (SL = 2) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 
R1
FC01:: /96
Source Node
CE1
R2
Transit Node
R3
Endpoint Node
FC03:: /96
FC04:: /96
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
FC01::1
FC03::3
FC04::4
FC01:: /96
FC01::1
Locator
End SID
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 30: Endpoint Node
An endpoint node is a node that receives an SRv6 packet destined for itself (a packet of which the IPv6 destination address is a local SID).
For example, R3 searches its local SID table based on the IPv6 DA FC03::3 of the packet and finds a matching End SID. Then, R3 decrements the SL value by 1, uses the SID whose SL value is 1 as the destination IPv6 address, searches the routing table, and forwards the packet.
There may be multiple endpoint nodes on the data forwarding path. Each endpoint node provides services such as packet forwarding, encapsulation, and decapsulation.
IPv6 Header |  | 
SRH (SL = 1) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 
R1
FC01:: /96
Source Node
CE1
R2
Transit Node
R3
Endpoint Node
FC03:: /96
FC04:: /96
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
FC01::1
FC03::3
FC04::4
FC01:: /96
FC01::1
Locator
End SID
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: Each SRv6 node maintains a local SID table that contains all SRv6 SIDs generated on the node, and an SRv6 FIB can be generated based on the table. The local SID table provides the following functions:
  Defines locally generated SIDs, such as End.X SIDs.
  Specifies instructions bound to the SIDs.
  Stores forwarding information related to the instructions, such as outbound interface and next hop information.

## Slide 31: SRv6 Forwarding Modes
SRv6 supports two forwarding modes: SRv6 Policy and SRv6 BE.
  In addition to implementing traffic engineering, SRv6 Policy can work with a controller to meet differentiated service requirements more effectively, achieving a service-driven network.
  SRv6 BE is a simplified implementation of SRv6. Typically, it can provide only best-effort forwarding and does not involve SRHs.
In the initial phase of SRv6 deployment, SRv6 BE can be used to quickly provision services based on IPv6 route reachability, offering unparalleled advantages. During future evolution, transit nodes can be upgraded on demand and SRv6 Policy can be deployed to meet the requirements of high-value services.
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 32: SRv6 Locator Information Propagation
No matter whether traffic is forwarded in SRv6 BE or SRv6 Policy mode, a router can forward SRv6 packets only after obtaining SRv6 locator-related routing information.
SRv6 nodes usually use an extended IGP (extended OSPFv3 or IS-IS) to propagate locator-related routing information to network nodes, including the source, transit, and endpoint nodes.
R1
Source Node
R2
Transit Node
R3
Endpoint Node
R4
Endpoint Node
IPv6 Routing Table
Dest Len NHP
FC01:: 96 Local
FC03:: 96 R2
FC04:: 96 R2
FC05:: 96 R2
IGP
IGP
IGP
R5
Endpoint Node
IPv6 Routing Table
Dest Len NHP
FC01:: 96 R1
FC03:: 96 R3
FC04:: 96 R3
FC05:: 96 R3
IPv6 Routing Table
Dest Len NHP
FC01:: 96 R2
FC03:: 96 Local
FC04:: 96 R4
FC05:: 96 R4
IPv6 Routing Table
Dest Len NHP
FC01:: 96 R3
FC03:: 96 R3
FC04:: 96 Local
FC05:: 96 R5
IPv6 Routing Table
Dest Len NHP
FC01:: 96 R4
FC03:: 96 R4
FC04:: 96 R4
FC05:: 96 Local
IGP
FC01:: /96
FC01::1
FC01:: /96
FC01::1
Locator
End SID
FC03:: /96
FC03::3
FC04:: /96
FC04::4
FC05:: /96
FC05::5
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 33: Forwarding in SRv6 BE Mode
Traditional MPLS involves two control protocols: LDP and RSVP-TE. The former uses IGP path computation results to establish LDP LSPs and guide traffic forwarding, but it does not support traffic engineering. Similar to LDP, SRv6 BE uses only one service SID to guide packet forwarding on an IP network in best-effort mode.
In SRv6 BE mode, the forwarding path is computed based on the IGP cost.
R1
Source Node
R2
R3
Endpoint Node
R4
Endpoint Node
R5
Endpoint Node
Transit Node
DIPv6: FC05::5 SIPv6: FC01::1
Payload
FC01:: /96
FC01::1
FC03:: /96
FC03::3
FC04:: /96
FC04::4
FC05:: /96
FC05::5
FC01:: /96
FC01::1
Locator
End SID
FC02:: /96
FC02::2
DIPv6: FC05::5 SIPv6: FC01::1
Payload
DIPv6: FC05::5 SIPv6: FC01::1
Payload
DIPv6: FC05::5 SIPv6: FC01::1
Payload
SRv6 SRH
SRv6 Node
SRv6 Forwarding

## Slide 34: Forwarding in SRv6 Policy Mode
In SRv6 forwarding, each time a packet passes through an SRv6 endpoint node, the SL field is decremented by 1 and the IPv6 DA in the IPv6 header changes. The SL and Segment List fields are both used to determine an IPv6 DA.
Different from SR-MPLS label processing, SRv6 SRH processing is implemented from the bottom up, and segments in the SRv6 SRH are not popped after being processed by a node. Therefore, the SRv6 header can be used for path backtracking.
R1
Source Node
R2
R3
Endpoint Node
R4
Endpoint Node
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 2) FC05::5 FC04::4 FC03::3
Payload
R5
Endpoint Node
DIPv6: FC04::4 SIPv6: FC01::1
SRH (SL = 1) FC05::5 FC04::4 FC03::3
Payload
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 2) FC05::5 FC04::4 FC03::3
Payload
Transit Node
DIPv6: FC05::5 SIPv6: FC01::1
Payload
FC01:: /96
FC01::1
FC03:: /96
FC03::3
FC04:: /96
FC04::4
FC05:: /96
FC05::5
FC01:: /96
FC01::1
Locator
End SID
DIPv6: FC05::5 SIPv6: FC01::1
SRH (SL = 0) FC05::5 FC04::4 FC03::3
Payload
If the type of the SID whose SL value is 0 is End, End.X, or End.DT, the SRH is removed on the penultimate segment by default.
FC02:: /96
FC02::2
SRv6 SRH
SRv6 Node
SRv6 Forwarding
Notes: In MPLS, different removal options are defined using the Implicit-Null and Non-null options. Penultimate hop popping (PHP) in the MPLS data plane refers to the process in which the outermost label of the MPLS label stack is removed by an LSR before the packet reaches the adjacent label edge router (LER). If PHP is not enabled on the MPLS network, the LER is responsible for removing the label.
These behaviors are defined as two functions in SRv6: PSP and USP.

## Slide 35
SRv6 Overview
SRv6 Fundamentals
  Basic Concepts of SRv6
  SRv6 Policy Path Establishment and Traffic Steering
  Typical SRv6 Applications
SRv6 High Reliability
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 36: SRv6 Policy Overview
SRv6 Policy is a new traffic steering technology developed based on SRv6.
An SRv6 Policy is a set of candidate paths consisting of one or more segment lists, that is, SID lists. Each SID list identifies an E2E path from the source to the destination, instructing a device to forward traffic through the path rather than the shortest path computed using an IGP.
If a packet is steered into an SRv6 Policy, the headend adds a SID list into the packet, and other devices receiving the packet execute the instructions encapsulated into the list.
Notes: https://datatracker.ietf.org/doc/draft-ietf-spring-segment-routing-policy/

## Slide 37: SRv6 Policy Identification
An SRv6 Policy is identified by the tuple <headend, color, endpoint>.
For an SRv6 Policy with a specified headend, it is identified only using <color, endpoint>.
  Headend: node where an SRv6 Policy is originated. Generally, it is a globally unique IP address.
  Color: 32-bit extended community attribute. It is used to identify a type of service intent (e.g. low delay).
  Endpoint: destination address of an SRv6 Policy. Generally, it is a globally unique IPv6 address.
On the specified headend, the color and endpoint are used to identify the forwarding path of the corresponding SRv6 Policy.
Endpoint 1
Endpoint 2
Color 15
Color 20
Color 25
SRv6 Policy 1 <color 15, endpoint 1>
SRv6 Policy 2 <color 20, endpoint 2>
SRv6 Policy 3 <color 25, endpoint 2>
Color 20
Notes: An endpoint in an SRv6 Policy is different from an endpoint node in SRv6.
  The endpoint node in SRv6 refers to the type of the device that processes the SRH.
  The endpoint in an SRv6 Policy refers to the policy's egress, which is generally expressed using an IPv6 address.

## Slide 38: SRv6 Policy Path Model
One SRv6 Policy may contain multiple candidate paths with the preference attribute. The valid candidate path with the highest preference functions as the primary path of the SRv6 Policy, and the valid candidate path with the second highest preference functions as a backup path.
A candidate path is an SRv6 Policy's basic unit that is manually configured or is sent to the headend through BGP IPv6 SR Policy.
Weights can be configured for segment lists to control load balancing among SRv6 paths.
SRv6 Policy
Candidate path 1
Preference 200
Candidate path 2
Preference 100
Segment list 1
Weight
Segment list 2
Weight
Segment list 1
Weight
Primary path
Backup path
SR Policy P1 <headend, color, endpoint>
Candidate-path CP1 <protocol, origin, discriminator>
Preference 200
Weight W1, SID-List1 <SID11...SID1i>
Weight W2, SID-List2 <SID21...SID2j>
Candidate-path CP2 <protocol, origin, discriminator>
Preference 100
Weight W3, SID-List3 <SID31...SID3i>
Weight W4, SID-List4 <SID41...SID4j>
<Headend, color, endpoint>
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: SR Policy P1 is uniquely determined by the triplet <headend, color, endpoint>.
An SR Policy can contain multiple candidate paths (e.g. CP1 and CP2). Each of the paths is uniquely determined by the triplet <protocol, origin, discriminator>.
CP1 is the primary path because it is valid and has the highest preference. The two SID lists of CP1 are delivered to the forwarder, and traffic is balanced between the two paths based on weights. For the SID list <SID11...SID1i>, traffic is balanced according to W1/(W1+W2).

## Slide 39: Overview of SRv6 Policy Path Establishment
In Huawei's SRv6 Policy solution architecture, the controller (iMaster NCE-IP) is used to establish SRv6 Policy paths.
  The controller uses BGP-LS to collect topology information collected through an extended IGP to compute SRv6 Policy paths and display state information.
  The controller uses BGP IPv6 SR Policy to deliver SRv6 Policy information (e.g. headend, color, and endpoint) to the headend.
Huawei's SRv6 Policy solution also uses NETCONF to deliver other configurations, such as service interfaces and route-policies (with the color attribute).
In addition to delivering SRv6 Policies through iMaster NCE-IP, you can also manually deploy SRv6 Policies.
1. BGP-LS
Color
Headend
Endpoint
2. BGP IPv6 SR Policy
3. NETCONF
Extended IS-IS
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: Mainstream methods for SRv6 Policy implementation:
  BGP: BGP-LS is used to collect topology information, so that no new interface protocol needs to be introduced for customer-developed controllers. BGP IPv6 SR Policy is used to deliver route information.
  PCEP: is a mature southbound protocol used in SR-MPLS TE scenarios. However, the tunnel implementation models of vendors are different and cannot interwork, and the interaction process of PCEP is more complex than that of BGP. As such, BGP extension is recommended.
  NETCONF/YANG: delivers tunnel paths to forwarders as configurations. This method is not recommended because it delivers configurations in essence and offers the poorest performance. In a comprehensive solution, NETCONF is used to deliver configurations other than tunnel configurations.
Huawei devices mainly use BGP to deploy SRv6 Policies.

## Slide 40: Information Collection Through BGP-LS
In Huawei's SRv6 Policy solution architecture, BGP-LS mainly provides the following functions:
  Advertises the topology, prefix, SRv6 locator, and SID information collected by IS-IS/OSPFv3 to iMaster NCE-IP through BGP-LS routes.
  Advertises the SRv6 Policy status through BGP-LS routes.
RR
PE1
PE2
P1
PE4
PE3
BGP-LS
SRv6 Policy
BGP-LS peer
[~PE1]display bgp link-state unicast routing-table
Total Number of Node Routes: 36
*> Network : [NODE][ISIS-LEVEL-2][IDENTIFIER0][LOCAL[as65001][bgp-ls-identifier1.0.0.1][ospf-area-id0.0.0.0][igp-router-id0010.0000.0001.00]] //Topology node information
*> Network : [LINK][ISIS-LEVEL-2][IDENTIFIER0][LOCAL[as65001][bgp-ls-identifier1.0.0.1][ospf-area-id0.0.0.0][igp-router-id0010.0000.0001.00]][REMOTE[as65001][bgp-ls-identifier1.0.0.1][ospf-area-id0.0.0.0][igp-router-id0010.0000.0002.00]][LINK[if-address10.0.0.26][peer-address10.0.0.25][if-address::][peer-address::]] //Topology link information
*> Network : [SRV6-SID][ISIS-LEVEL-2][IDENTIFIER0][LOCAL[as65001][bgp-ls-identifier1.0.0.1][ospf-area-id0.0.0.0][igp-router-id0010.0000.0006.00]][SID[mt-id2][sidFC00:6::1]] //SRv6 SID information
*> Network : [TEPOLICY][SEGMENT-ROUTING][IDENTIFIER0][LOCAL[as65001][bgp-ls-identifier1.0.0.1][bgp-router-id1.0.0.1][ipv4-router-id0.0.0.0][ipv6-router-idFC01::1]][TE[protocol-origin2][Flag128][endpointFC01::4][color16][originator-as65001][originator-address172.21.17.102][discriminator49]] //SRv6 Policy status
Color 16
Loopback
FC01::4
IS-IS System ID
0010.0000.0001.00
IS-IS System ID
0010.0000.0002.00
End SID
FC00:6::1
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: BGP-LS connection:
  Collects tunnel topology information for SR Policy path computation.
  BGP-LS supports the collection of SR Policy status information, based on which the controller displays tunnel status. https://datatracker.ietf.org/doc/draft-ietf-idr-te-lsp-distribution/
  BGP-LS supports SRLB information encapsulation and decapsulation, so that the controller can obtain the SRLB information for binding SID allocation. (The backup path of each SR Policy corresponds to a binding SID.)
  BGP-LS also needs to be deployed on the headend to advertise the SRv6 Policy status.

## Slide 41: Path Delivery Through BGP IPv6 SR Policy
iMaster NCE-IP can deliver an SRv6 Policy to the specified headend through the BGP IPv6 SR Policy peer relationship.
An SRv6 Policy is represented as [distinguisher][color][endpoint] in the BGP routing table.
RR
PE1
PE2
P1
PE4
PE3
Color 16
Loopback
FC01::4
[~PE1]display bgp sr-policy ipv6 routing-table [49][16][FC01::4]
BGP local router ID : 1.0.0.1
Local AS number : 65001
Paths: 2 available, 1 best, 1 select, 0 best-external, 0 add-path
BGP routing table entry information of [49][16][FC01::4]:
...
Tunnel Encaps Attribute (23):
Tunnel Type: SR Policy (15)
Preference: 10
Binding SID: FC00:1::1:1, s-flag(0), i-flag(0)
Segment List
Weight: 1
Path MTU: 9600
Segment: type:2, SID: FC00:5::1
Segment: type:2, SID: FC00:6::1
Segment: type:2, SID: FC00:6::1:60
Template ID: 4294967278
Not advertised to any peer yet
BGP IPv6 SR-Policy
Headend
End SID
FC00:5::1
End SID
FC00:6::1
End.X SID
FC00:6::1:60
DIPv6: FC00:5::1 SIPv6: FC00:1::1
SRH (SL = 2) FC00:6::1:60 FC00:6::1 FC00:5::1
Payload
SRv6 Policy
BGP SR-Policy peer
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: BGP IPv6 SR Policy connection:
  The controller delivers SRv6 Policy information to forwarders for SRv6 Policy generation.
  BGP routes delivered by the controller carry the color community attribute, which can be transmitted. The headend finds a matching BGP route and recurses it to the corresponding SRv6 Policy based on the color and endpoint information.
  In Huawei's SRv6 Policy solution, path computation constraints of each application need to be uniformly planned on the controller based on SLAs, and different colors are used to identify SRv6 Policies. An SRv6 Policy is uniquely identified by <headend, color, endpoint>. The BGP route of services to be steered into an SRv6 Policy needs to carry the corresponding color attribute.
Binding SIDs are mainly used for path stitching.

## Slide 42: Inter-AS SRv6 Policy Path Establishment
SRv6 devices need to obtain network-wide SIDs to implement E2E data forwarding.
In an AS, devices can use an extended IGP (extended OSPFv3 or IS-IS) to obtain intra-AS SID information. In inter-AS scenarios, however, BGP egress peer engineering (EPE) needs to be used to transmit SID information.
AS 65001
AS 65002
IGP route (carrying SRv6-related route information)
IGP route (carrying SRv6-related route information)
Mutual route import between IS-IS and BGP processes
BGP EPE
IS-IS
IS-IS
Mutual route import between IS-IS and BGP processes
End.X SID
BGP route (carrying SRv6-related route information)
DIPv6: FC02::2 SIPv6: FC01::1
SRH (SL = 3) FC04::4 FC03::3 FC02::1C FC02::2
Payload
DIPv6: FC02::1C SIPv6: FC01::1
SRH (SL = 2) FC04::4 FC03::3 FC02::1C FC02::2
Payload
DIPv6: FC04::4 SIPv6: FC01::1
SRH (SL = 0) FC04::4 FC03::3 FC02::1C FC02::2
Payload
FC02::1C
FC01::1
FC02::2
FC03::1C
FC02::1B
FC03::1B
FC03::3
FC04::4
FC02::1C
FC02::2
End SID
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 1) FC04::4 FC03::3 FC02::1C FC02::2
Payload
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: BGP EPE can allocate BGP peer SIDs to inter-AS paths. Peer SIDs are classified into the following types:
  A Peer-Node SID identifies a peer node. The peers at both ends of each BGP session are allocated with Peer-Node SIDs. An EBGP peer relationship established based on loopback interfaces may traverse multiple physical links. In this case, the Peer-Node SID of a peer is mapped to multiple outbound interfaces. Peer-Node SIDs are End SIDs.
  A Peer-Adj SID identifies an adjacency to a peer. An EBGP peer relationship established based on loopback interfaces may traverse multiple physical links. In this case, each adjacency is allocated with a Peer-Adj SID. Only the specified link (mapped to the specified outbound interface) can be used for forwarding. Peer-Adj SIDs are End.X SIDs.
BGP EPE allocates SIDs only to BGP peers and links, but cannot be used to construct a forwarding path. BGP peer SIDs must be used with IGP SIDs to form an E2E path.

## Slide 43: SRv6 Policy Path Stitching (1)
Due to the restrictions on the stack depth in the SRv6 SRH, SRv6 path stitching can be deployed on large networks.
Path stitching is mainly implemented using stitching SIDs and nodes.
  A stitching SID (also called binding SID) can be used to represent an SRv6 Policy's forwarding path.
  A stitching node, which is generally an ABR or ASBR, is responsible for processing the binding SID and adding SRH information.
AS 65001
AS 65002
SRH (SL = 3) Segment List (0) Segment List (1) Segment List (2) Segment List (3)
Stack depth
CE1
PE1
ASBR2
PE2
ASBR1
CE2
End.X SID
FC02::1C
FC03::4
End SID
FC01::1
FC02::2
FC03::3
FC04::4
FC02::1C
FC03::1C
FC03::100
Binding SID
IPv6 Header
SRH (SL = 3) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
FC04::100
End.DT4 SID
FC04::100
FC03::100
The stack depth cannot accommodate the E2E segment list.
IPv6 Header
SRH (SL = 2) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 1) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 0) FC04::4
SRH (SL = 0) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 0) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
CE1->CE2
CE1->CE2
Assume that the stack depth supported by the device is 4.
Sent from PE1
Internal processing on ASBR1
Internal processing on ASBR1
Sent from ASBR2
Internal processing on PE2
Insert mode
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: On a large network, the SRv6 SRH may be of a large size. Considering device limitations and forwarding efficiency, the number of SIDs in the SRH must be limited.
Generally, there are two methods for reducing the SRH size:
  SRv6 header compression
    Huawei mainly uses the G-SRv6 solution for SRv6 header compression, reducing the SRH size and improving the forwarding efficiency without sacrificing SID information.
    This course will not cover relevant header compression technologies.
  SRv6 path stitching
    Binding SIDs are used to stitch different SRv6 paths together, so that the SRH of each SRv6 path is not too large.
The SRv6 stack depth is generally determined by device capabilities.
SRv6 mainly supports the following four types of binding SIDs:
  End.B6.Insert
  End.B6.Insert.Red
  End.B6.Encaps
  End.B6.Encaps.Red

## Slide 44: SRv6 Policy Path Stitching (2)
Main encapsulation modes supported by SRv6 stitching labels:
  Insert mode: inserts an SRH after the original IPv6 header so that the packet is forwarded based on the original IPv6 header and the new SRH.
  Encaps mode: inserts an outer IPv6 header and SRH before the original IPv6 header so that the packet is forwarded based on the outer IPv6 header and SRH.
AS65001
AS65002
SRH (SL = 3) Segment List (0) Segment List (1) Segment List (2) Segment List (3)
Stack depth
CE1
PE1
ASBR2
PE2
ASBR1
CE2
End.X SID
FC02::1C
FC03::4
End SID
FC01::1
FC02::2
FC03::3
FC04::4
FC02::1C
FC03::1C
FC03::100
Binding SID
IPv6 Header
SRH (SL = 3) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
FC04::100
End.DT4 SID
FC04::100
FC03::100
The stack depth cannot accommodate the E2E segment list.
IPv6 Header
SRH (SL = 2) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 1) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 0) FC04::4
IPv6 Header
SRH (SL = 0) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
IPv6 Header
SRH (SL = 0) FC04::100 FC03::100 FC02::1C FC02::2
CE1->CE2
CE1->CE2
CE1->CE2
Assume that the stack depth supported by the device is 4.
Sent from PE1
Internal processing on ASBR1
Internal processing on ASBR1
Sent from ASBR2
Internal processing on PE2
Encaps mode
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: The End.B6.Encaps instruction used in Encaps mode can be disassembled into End + B6 + Encaps, where B6 indicates the application of an SRv6 Policy and Encaps indicates the encapsulation of an outer IPv6 header and SRH. This instruction includes the following operations: decrements the SL value of the inner SRH by 1, copies the SID to which the SL field is pointing to the DA field of the inner IPv6 header, encapsulates an IPv6 header and SRH (including segment lists), sets the source address to the address of the current node and the destination address to the first SID of the involved SRv6 Policy, sets other fields in the outer IPv6 header, looks up the corresponding table, and forwards the new IPv6 packet accordingly.

## Slide 45: Color-based Traffic Steering to SRv6 Policies
SRv6 Policies support color-based traffic steering, enabling traffic to be steered to an SRv6 Policy through route recursion that is implemented based on the color value and destination address in the route.
Color: 15
PE1
PE2
Color: 20
CE1
Net1
BGP Route
Prefix NHP Ext-Community
Net1 PE2 0:15
Net2 PE2 0:20
IGP Route
Prefix NHP
Net1 CE2
Net2 CE2
IGP Route
Prefix NHP
Net1 PE1
Net2 PE1
Net2
CE2
Use route-policies to specify color values (extended community attribute) for specific BGP routes.
When forwarding a packet, the PE determines the SRv6 Policy to which the corresponding route recurses based on the destination address of the packet and the next hop of the route.
DIP: Net1
DIP: Net2
Alternatively, deploy an export route-policy.
Alternatively, deploy an import route-policy.
PE1
VRF1
VRF2
SRv6 Policy
SRv6 Policy
15
20
Alternatively, specify color values for specific VRFs.
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: Configure a tunnel policy on PE1. After receiving the BGP routes (Net1 and Net2), PE1 recurses the routes to different SRv6 Policies based on the color values (0:15 and 0:20) and the next hop (PE2). Before forwarding packets to specified subnets (Net1 and Net2), PE1 adds specific SRv6 SID stacks to the packets.
The color attribute in route entries can be modified before the local router (for example, PE2) sends routes or after the peer router (for example, PE1) receives routes.
You can also directly configure the color attribute for the VPN instance of the originating router (for example, PE1), so that all traffic of the VPN instance is forwarded over the specified SRv6 Policy.

## Slide 46: DSCP-based Traffic Steering to SRv6 Policies
Color-based traffic steering causes different traffic (such as HTTP and FTP traffic) destined for the same address to recurse to the same forwarding path, leading to a failure to implement refined traffic control. In this case, DSCP-based traffic steering can be performed to recurse traffic to different forwarding paths.
Color: 15
PE1
PE2
Color: 20
CE1
Net1
BGP Route
Prefix NHP Ext-Community
Net1 PE2 0:1000
IGP Route
Prefix NHP
Net1 CE2
IGP Route
Prefix NHP
Net1 PE1
CE2
Use a route-policy to specify a color value (extended community attribute) for the specific BGP route.
PE1 finds a matching mapping policy (color 1000) based on the packet destination address and next hop, and then recurses the packets to different forwarding paths based on DSCP values.
DIP: Net1, DSCP: 46
DIP: Net1, DSCP: 23
HTTP service
FTP service
Mapping policy (Color 1000)
SRv6 Policy 1
(Color 15)
SRv6 Policy 2 (Color 20)
PE1
Destination address
Next hop
DSCP 24
DSCP 28
Alternatively, deploy an export route-policy.
Alternatively, deploy an import route-policy.
PE1
VRF1
SRv6 Policy
1000
Alternatively, specify a color value for the specific VRF.
SRv6 Policy Path Establishment
Traffic Steering to SRv6 Policies
Notes: In DSCP-based traffic steering, the color attribute in route entries is mainly used to find a matching mapping policy.
The color attribute in route entries can be modified in the outbound direction of the originating router (for example, PE2) or in the inbound direction of the receiving router (for example, PE1).
You can also directly configure the color attribute for the VPN instance of the originating router (for example, PE1), so that all traffic of the VPN instance is forwarded over the specified SRv6 Policy.

## Slide 47
SRv6 Overview
SRv6 Fundamentals
  Basic Concepts of SRv6
  SRv6 Policy Path Establishment and Traffic Steering
  Typical SRv6 Applications
SRv6 High Reliability
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 48: L3VPN over SRv6 Policy
If an SRv6 Policy is used to carry VPN traffic, the last-hop SRv6 device processes data in a way slightly different from that of a common SRv6 device.
PE1
CE1
P1
PE2
CE2
End.DT4
FC03::300
VPNA
VPNA
65000
DIP: Net2 SIP: CE1
Payload
DIPv6: FC02::2 SIPv6: FC01::1
SRH (SL = 2) FC03::300 FC03::3 FC02::2
DIP: Net2 SIP: CE1
Payload
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 1) FC03::300 FC03::3 FC02::2
DIP: Net2 SIP: CE1
Payload
DIPv6: FC03::300 SIPv6: FC01::1
SRH (SL = 0) FC03::300 FC03::3 FC02::2
DIP: Net2 SIP: CE1
Payload
DIP: CE2 SIP: CE1
Payload
Forwards the IP packet over the corresponding SRv6 Policy based on the color value.
Forwards the packet based on the outer IPv6 header.
Removes the outer IPv6 header and forwards the packet as a common IP one.
The last-hop SRv6 router looks up the routing table twice.
FC01:: /96
FC01::1
FC02:: /96
FC02::2
FC03:: /96
FC03::3
FC01:: /96
FC01::1
Locator
End SID
MP-BGP Route
Prefix NHP Ext-Community
Net2 PE2 FC03::300 + 0:15 + RT
IGP Route
Prefix NHP
Net2 CE2
IGP Route
Prefix NHP
Net2 PE1
Net2
Color 15
Notes: Route advertisement process:
  SRv6 and SRv6 VPN are configured on each PE, and IPv6 or SRv6 is enabled on the transit node.
  PE2 advertises an SRv6 locator route to PE1.
  CE-to-PE route advertisement: CE2 advertises its route to PE2. Either a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP) can be deployed between the CE and PE.
  After learning the route advertised by CE2, PE2 installs it in the routing table of the corresponding VPN instance and converts the route into an MP-BGP one.
  Inter-PE route advertisement: Configure a BGP or VPN export policy on PE2 (or a BGP or VPN import policy on PE1), and set a color value for the route (next hop: PE2). Then, configure PE2 to send routing information to PE1 through a BGP peer relationship using update messages with RT and SRv6 VPN SID attributes.
  After PE1 receives the VPN route, if the next hop in the route is reachable and the route matches the BGP import policy, PE1 performs a series of actions to determine whether to install the route in the routing table of the corresponding VPN instance. These actions include VPN route leaking, route recursion to an SRv6 path, and route selection. In this example, PE1 installs the VPN route, which is associated with the SRv6 VPN SID.
  PE-to-CE route advertisement: CE1 can learn the VPN route from PE1 through a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP). The route advertisement process is similar to that from CE2 to PE2.

## Slide 49
Notes: Packet forwarding process:
  After receiving a common unicast packet from CE1, PE1 searches the routing table of the corresponding VPN instance and finds that the outbound interface of the route is an SRv6 Policy interface. PE1 then inserts an SRH carrying the SID list of the SRv6 Policy and encapsulates an IPv6 header into the packet. After completing these operations, PE1 forwards the packet to P1.
  The transit node P1 forwards the packet hop by hop based on SRH information.
  After receiving the packet, the endpoint PE2 searches the My Local SID Table and finds an End SID that matches the IPv6 DA FC03::3 in the packet. According to the instruction bound to the SID, PE2 decrements the SL value of the packet by 1 and updates the IPv6 DA to the VPN SID FC03::300.
  Based on the VPN SID FC03::300, PE2 searches the My Local SID Table and finds a matching End.DT4 SID. According to the instruction bound to the SID, PE2 decapsulates the packet, removes the SRH and IPv6 header, searches the routing table of the VPN instance corresponding to the VPN SID FC03::300 according to the DA in the inner packet, and forwards the packet to CE2.

## Slide 50: L3VPN over SRv6 BE
When SRv6 BE is used to carry VPN traffic, the P between PEs does not function as an endpoint.
PE1
CE1
P1
PE2
CE2
End.DT4
FC03::300
VPNA
VPNA
65000
DIP: Net2 SIP: CE1
Payload
DIPv6: FC03::300 SIPv6: FC01::1
DIP: Net2 SIP: CE1
Payload
DIP: Net2 SIP: CE1
Payload
Forwards the IP packet over an SRv6 Policy.
PE2 removes the outer IPv6 header and forwards the packet as a common IP one.
DIPv6: FC03::300 SIPv6: FC01::1
DIP: Net2 SIP: CE1
Payload
Forwards the packet based on the outer IPv6 header.
FC01:: /96
FC01::1
Locator
End SID
FC01:: /96
FC01::1
FC02:: /96
FC02::2
FC03:: /96
FC03::3
MP-BGP Route
Prefix NHP Ext-Community
Net2 PE2 FC03::300 + RT
IGP Route
Prefix NHP
Net2 CE2
Net2
IGP Route
Prefix NHP
Net2 PE1
Notes: Route advertisement process:
  SRv6 and SRv6 VPN are configured on each PE, and IPv6 is enabled on the transit node.
  PE2 advertises an SRv6 locator route to PE1.
  CE-to-PE route advertisement: CE2 advertises its route to PE2. Either a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP) can be deployed between the CE and PE.
  After learning the route advertised by CE2, PE2 installs it in the routing table of the corresponding VPN instance and converts the route into an MP-BGP one.
  Inter-PE route advertisement: PE2 advertises the VPN route to egress node PE1 through MP-BGP using update messages with RT and SRv6 VPN SID attributes.
  After PE1 receives the VPN route, if the next hop in the route is reachable and the route matches the BGP import policy, PE1 performs a series of actions to determine whether to install the route in the routing table of the corresponding VPN instance. These actions include VPN route leaking, route recursion to an SRv6 BE path, and route selection. In this example, PE1 installs the VPN route, which is associated with the SRv6 VPN SID.
  PE-to-CE route advertisement: CE1 can learn the VPN route from PE1 through a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP). The route advertisement process is similar to that from CE2 to PE2.

## Slide 51
Notes: Packet forwarding process:
  After receiving a common unicast packet from CE1, PE1 searches the routing table of the corresponding VPN instance and finds that the outbound interface of the route is an SRv6 Policy interface. PE1 then inserts an SRH carrying the SID list of the SRv6 Policy and encapsulates an IPv6 header into the packet. After completing these operations, PE1 forwards the packet to P1.
  The transit node P1 forwards the packet hop by hop based on SRH information.
  After receiving the packet, the endpoint PE2 searches the My Local SID Table and finds an End SID that matches the IPv6 DA FC03::3 in the packet. According to the instruction bound to the SID, PE2 decrements the SL value of the packet by 1 and updates the IPv6 DA to the VPN SID FC03::300.
  Based on the VPN SID FC03::300, PE2 searches the My Local SID Table and finds a matching End.DT4 SID. According to the instruction bound to the SID, PE2 decapsulates the packet, removes the SRH and IPv6 header, searches the routing table of the VPN instance corresponding to the VPN SID FC03::300 according to the DA in the inner packet, and forwards the packet to CE2.

## Slide 52: Native IPv6 over SRv6 Policy
Common IPv6 data can also be carried using SRv6.
PE1
CE1
P1
PE2
CE2
65000
DIPv6: Net2 SIPv6: CE1
Payload
DIPv6: FC02::2 SIPv6: CE1
SRH (SL = 2) Net2 FC03::3 FC02::2
Payload
DIPv6: FC03::3 SIPv6: CE1
SRH (SL = 1) Net2 FC03::3 FC02::2
Payload
DIPv6: Net2 SIPv6: CE1
SRH (SL = 0) Net2 FC03::3 FC02::2
Payload
Forwards the IPv6 packet over the corresponding SRv6 Policy based on the color value.
Forwards the packet based on the outer IPv6 header.
Removes the SRH and forwards the packet as a common IPv6 one.
FC01:: /96
FC01::1
FC02:: /96
FC02::2
FC03:: /96
FC03::3
FC01:: /96
FC01::1
Locator
End SID
BGP Route
Prefix NHP Ext-Community
Net2 PE2 0:15
IGP Route
Prefix NHP
Net2 CE2
IGP Route
Prefix NHP
Net2 PE1
Net2
Color 15
DIPv6: Net2 SIPv6: CE1
Payload
Notes: Route advertisement process:
  SRv6 and SRv6 VPN are configured on each PE, and IPv6 or SRv6 is enabled on the transit node.
  PE2 advertises an SRv6 locator route to PE1.
  CE-to-PE route advertisement: CE2 advertises its route to PE2. Either a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP) can be deployed between the CE and PE.
  Inter-PE route advertisement: Configure a BGP export policy on PE2 (or a BGP import policy on PE1), and set a color value for the route (next hop: PE2). Then, configure PE2 to send routing information to PE1 through a BGP peer relationship.
  After PE1 receives the IPv6 route, if the next hop in the route is reachable and the route matches the BGP import policy, PE1 performs a series of actions, including route recursion to an SRv6 path and route selection.
  PE-to-CE route advertisement: CE1 can learn the IPv6 route from PE1 through a static route or a routing protocol (RIP, OSPFv3, IS-IS, or BGP). The route advertisement process is similar to that from CE2 to PE2.

## Slide 53
Notes: Packet forwarding process:
  After receiving a unicast IPv6 packet from CE1, PE1 searches the IPv6 routing table and finds that the outbound interface of the route is an SRv6 Policy interface. PE1 then inserts an SRH carrying the SID list of the SRv6 Policy and encapsulates an IPv6 header into the packet. After completing these operations, PE1 forwards the packet to P1.
  The transit node P1 forwards the packet hop by hop based on SRH information.
  After receiving the packet, the endpoint PE2 searches the My Local SID Table and finds an End SID that matches the IPv6 DA FC03::3 in the packet. According to the instruction bound to the SID, PE2 decrements the SL value of the packet by 1 and updates the IPv6 DA to the End SID Net2.
  Based on the End SID Net2, PE2 searches the My Local SID table, finds a matching End SID, removes the SRH and IPv6 header, and forwards the packet to CE2.

## Slide 54
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
  Overview of SRv6 High Reliability
  SRv6 Tunnel Status Detection and Tunnel Protection
  SRv6 Egress Protection and Access Protection
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 55: WAN Bearer Networks' Requirements for High Reliability
Fault recovery within 50 ms has become a basic requirement of WAN bearer networks.
  Voice services: have high requirements for real-time performance. If fault recovery is completed within milliseconds, the fault is imperceptible or only slightly perceptible to users, without much impacts on services. However, if the fault recovery time reaches seconds, the corresponding session is interrupted.
  IPTV services: If fault recovery is completed within milliseconds, IPTV services may encounter transient pixelation.
Slightly perceptible
Obviously perceptible
50 ms
Voice user experience
Imperceptible
0
500 ms
Impact of network faults on voice services
Reference standard:
YD/T 1071-2000 <IP Telephone Gateway technical specification>
2s
Session interrupted
I
I
B
B
B
B
B
B
P
P
GOP
I-frame damage caused by packet loss is the key cause of erratic display.
Impact of network faults on IPTV services

## Slide 56: Overview of Multi-Layer Reliability Solutions
WAN bearer networks require high reliability to be provided at device, network, and service layers to achieve E2E high availability of 99.999% and fast protection switching of all services within 50 ms.
EVPN L3VPN
Highly reliable hardware architecture: Key components, such as main control boards, SFUs, interface boards, power supply modules, and fans, adopt redundancy design.
Highly reliable networking architecture: effective redundant paths, reliable networking mode (e.g. ring, spine-leaf, or dual-plane networking), and sufficient protection bandwidth reserved.
TI-LFA, midpoint protection (TE FRR), and candidate path protection (HSB)
VPN FRR
Physical layer
Tunnel layer
Service layer
SRv6 tunnel
IGP

## Slide 57: Overview of Reliability Technologies for Multi-Layer Networks
Physical link
IGP
LSP
HSB
VPN
TI-LFA
BFD for interface
BFD for IGP
BFD for locator
SBFD for
SRv6 Policy
VPN FRR
Midpoint protection
Mixed VPN FRR
Microloop avoidance
Detection Object
Detection Technology
Protection Technology

## Slide 58: Usage Scenarios of Reliability Technologies for Multi-Layer Networks
Service Category | Protection Type | Tunnel Type | Failure Point | Detection Technology | Protection Technology | Specification
Common services | Local protection, E2E protection | SRv6 BE, SRv6 Policy | 4 to 8 | BFD for interface | 1. TI-LFA (SRv6 BE + SRv6 Policy) 2. Midpoint TI-LFA (SRv6 Policy) | 50 ms
 |  |  | 3 and 9 | BFD for locator | VPN FRR | 50 ms
 |  |  | 1, 2, 10, and 11 | BFD for interface | VPN mixed FRR, IP FRR | 50 ms
Services with high SLA requirements | Local protection, E2E protection | SRv6 Policy | 4 to 8 | SBFD for SRv6 Policy | HSB | 50 ms
 |  |  | 3 and 9 | SBFD for SRv6 Policy | VPN FRR | 200 ms/50 ms
 |  |  | 1, 2, 10, and 11 | BFD for interface | VPN mixed FRR, IP FRR | 50 ms
PE
PE
PE
P
P
CE
CE
CE
CE
PE
Bearer network
1
2
3
P
P
5
4
7
6
9
8
11
10
Access network
Intermediate network
Access network

## Slide 59
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
  Overview of SRv6 High Reliability
  SRv6 Tunnel Status Detection and Tunnel Protection
  SRv6 Egress Protection and Access Protection
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 60: SRv6 Tunnel Detection Technologies
SBFD can be used to detect tunnel connectivity in an E2E manner.
However, SBFD cannot detect the specific fault location on the network. As such, it is usually used with HSB or VPN FRR.
SRv6 tunnel connectivity can be detected using multiple technologies, such as SBFD, ping, and tracert.
SRv6 tunnel
SBFD
SBFD
Ping/Tracert
SRv6 SID ping is mainly used to check network connectivity and host reachability.
  Ping tests are classified into segment-by-segment tests and non-segment-by-segment tests.
In addition to checking network connectivity and host reachability, SRv6 SID tracert can be used to analyze the specific fault location on the network.
Tracert
SRv6 tunnel
Ping
Notes: Seamless bidirectional forwarding detection (SBFD) is a simplified BFD mechanism. With a simplified BFD state machine, SBFD shortens the negotiation time and improves network-wide flexibility.
  The IPv6 address of the SBFD reflector must be the same as the endpoint of the corresponding SRv6 Policy.
As SRv6 simply adds a new type of routing extension header to implement forwarding based on the IPv6 data plane, ICMPv6 ping and tracert can be directly used on an SRv6 network for connectivity check based on common IPv6 addresses, without requiring any changes to hardware or software. ICMPv6 ping and tracert both support packet forwarding to a destination address over the shortest path, thereby checking the reachability to the destination. If the destination address is an SRv6 SID, the check can be performed through either ICMPv6 ping & tracert or SRv6 OAM extensions. Currently, SRv6 OAM can be extended in either of the following ways:
  Set the O-bit (OAM bit) in the SRH.
  Insert an End.OP SID into the SRH.

## Slide 61: SBFD Implementation
Detection end
(Initiator)
Reflector
SBFD Control packet
SBFD Control packet
Down
Down -> Up
Before link detection, an SBFD initiator and an SBFD reflector exchange SBFD Control packets to notify each other of SBFD parameters (for example, discriminators). In link detection, the initiator proactively sends an SBFD packet, and the reflector loops this packet back. The initiator then determines the local status based on the looped packet.
Down
Up
Up
Admin Down
(Timer)
Admin Down
(Timer)
Up
The loopback packet constructed by the reflector carries the Admin Down or Up field.
After receiving a reflected packet carrying the Up state, the initiator sets the local state to Up. After receiving a reflected packet carrying the Admin Down state, it sets the local state to Down. It also sets the local state to Down if it does not receive any reflected packet before the timer expires.
SBFD State Machine on the Initiator
Notes: Because the state machine has only Up and Down states, the initiator can send packets carrying only the Up or Down state and receive packets carrying only the Up or Admin Down state. The initiator starts by sending an SBFD packet carrying the Down state to the reflector. The destination and source port numbers of the packet are 7784 and 4784, respectively; the destination IP address is a user-configured address on the 127 network segment; the source IP address is the locally configured LSR ID.
The reflector does not have any SBFD state machine or detection mechanism. For this reason, it does not proactively send SBFD Echo packets, but rather, it only reflects SBFD packets. The destination and source port numbers in the looped-back packet are 4784 and 7784, respectively; the source IP address is the locally configured LSR ID; the destination IP address is the source IP address of the initiator.

## Slide 62: Introduction to SRv6 Ping and Tracert
Version | Traffic Class |  | Flow Label |  | 
Payload Length |  |  |  | Next Header=43 | Hop Limit
IPv6 source address (SA) |  |  |  |  | 
IPv6 destination address (DA) |  |  |  |  | 
Next Header |  | Hdr Ext Len |  | Routing Type=4 | Segments Left=2
Last Entry |  | Flags |  | Tag | 
Segment List [0] |  |  |  |  | 
Segment List [1] |  |  |  |  | 
Segment List [2] |  |  |  |  | 
Optional TLV objects |  |  |  |  | 
L2/L3 Payload |  |  |  |  | 
O
Reserved
Solution 1: O-bit in the SRH
Because the O-bit is carried in the SRH, each SRv6 endpoint node needs to process and respond to ICMPv6 ping and tracert requests. Therefore, segment-by-segment tests can be implemented based on the O-bit.
Format of the Flags Field
Solution 2: End.OP SID
The End.OP SID can instruct data packets to be sent to the control plane for OAM processing.
In the case of an SRv6 Policy test, the headend encodes an End.OP SID into the segment list.
Because only the SRv6 endpoint that has generated an End.OP SID can process ICMPv6 ping and tracert request packets, E2E tests can be implemented based on End.OP SIDs.
00100000
Notes: Currently, SRv6 ping and tracert can be implemented using the following two methods:
  One method is to use the O-bit (OAM bit) in the SRH. Because the O-bit is carried in the SRH, each SRv6 endpoint node needs to process and respond to ICMPv6 ping and tracert requests. Therefore, segment-by-segment tests can be implemented based on the O-bit. You can run the ping ipv6-sid and tracert ipv6-sid commands to initiate tests based on one or more SIDs.
  The other method is to introduce End.OP SIDs, which instruct data packets to be sent to the control plane for OAM processing. In the case of an SRv6 Policy test, the headend encodes an End.OP SID into the segment list. Because only the SRv6 endpoint that has generated an End.OP SID can process ICMPv6 ping and tracert request packets, E2E tests can be implemented based on End.OP SIDs.
    For SID stack-based tests, specify one or more End.OP SIDs in the ping ipv6-sid and tracert ipv6-sid commands.
    For SRv6 Policy-based tests, specify the end-op parameter in the ping srv6-te policy and tracert srv6-te policy commands.

## Slide 63: SRv6 Ping Implementation
SRv6 ping can be classified into segment-by-segment ping and non-segment-by-segment ping.
PE1
P1
PE2
FC01::1
FC02::2
FC03::3
DIPv6: FC02::2 SIPv6: FC01::1
SRH (SL = 1) FC03::3 FC02::2
ICMPv6 Request
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 0) FC03::3 FC02::2
ICMPv6 Request
DIPv6: FC01::1 SIPv6: FC02::2
ICMPv6 Reply
Segment-by-segment ping test
Non-segment-by-segment ping test
PE1
P1
PE2
FC01::1
FC02::2
FC03::3
DIPv6: FC02::2 SIPv6: FC01::1
SRH (SL = 1) FC03::3 FC02::2
ICMPv6 Request
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 0) FC03::3 FC02::2
ICMPv6 Request
DIPv6: FC01::1 SIPv6: FC03::3
ICMPv6 Reply
DIPv6: FC01::1 SIPv6: FC03::3
ICMPv6 Reply
Notes: For a segment-by-segment test:
  PE1 initiates a ping operation to PE2. Specifically, it constructs an ICMPv6 Request packet carrying the SRv6 SIDs (End and End.X SIDs) of P1 and the End SID of PE2 and then forwards the packet.
  After receiving the ICMPv6 Request packet, P1 sends an ICMPv6 Reply packet to PE1 and forwards the ICMPv6 Request packet to PE2.
  After receiving the ICMPv6 Request packet, PE2 sends an ICMPv6 Reply packet to PE1.
For a non-segment-by-segment test:
  PE1 initiates a ping operation to PE2. Specifically, it constructs an ICMPv6 Request packet carrying the End SID of PE2 and then forwards the packet.
  After receiving the ICMPv6 Request packet, P1 forwards it to PE2.
  After receiving the ICMPv6 Request packet, PE2 sends an ICMPv6 Reply packet to PE1. In this case, you can view detailed information about the ping operation on PE1.

## Slide 64: SRv6 Tracert Implementation
SRv6 tracert can be classified into overlay tracert and non-overlay tracert.
PE1
P1
PE2
FC01::1
FC02::2
FC03::3
DIPv6: FC02::2 SIPv6: FC01::1 TTL=63
SRH (SL = 1) FC03::3 FC02::2
UDP
DIPv6: FC03::3 SIPv6: FC01::1 TTL=62
SRH (SL = 0) FC03::3 FC02::2
UDP
DIPv6: FC01::1 SIPv6: FC02::2
ICMP Port-Unreachable
PE1
P1
PE2
FC01::1
FC02::2
FC03::3
DIPv6: FC02::2 SIPv6: FC01::1 TTL=0
SRH (SL = 1) FC03::3 FC02::2
UDP
DIPv6: FC01::1 SIPv6: FC02::2
ICMPv6 Time Exceeded
Overlay tracert test
Non-overlay tracert test
DIPv6: FC01::1 SIPv6: FC03::3
ICMP Port-Unreachable
DIPv6: FC02::2 SIPv6: FC01::1 TTL=1
SRH (SL = 1) FC03::3 FC02::2
UDP
DIPv6: FC03::3 SIPv6: FC01::1 TTL=0
SRH (SL = 0) FC03::3 FC02::2
UDP
DIPv6: FC01::1 SIPv6: FC03::3
ICMP Port-Unreachable
Notes: For an overlay test:
  PE1 initiates a tracert operation to PE2. Specifically, it constructs a UDP packet carrying the SRv6 SIDs (End and End.X SIDs) of P1 and the End SID of PE2, encapsulates an SRH into the packet, and then forwards the packet. In this case, the value of the Hop Limit field (equal to the TTL field in IPv4) in the IPv6 header is set to 64 and decrements by 1 each time the packet passes through a device. When the value of the Hop Limit field is 0, the packet is discarded, and then an ICMPv6 Time Exceeded message is sent to PE1.
  After receiving the UDP packet, P1 changes the value of the Hop Limit field to 63, sends an ICMPv6 Port Unreachable message to PE1, and forwards the UDP packet to PE2.
  After receiving the UDP packet, PE2 changes the value of the Hop Limit field to 62 and sends an ICMPv6 Port Unreachable message to PE1.

## Slide 65
Notes: For a non-overlay test:
  PE1 initiates a tracert operation to PE2. Specifically, it constructs a UDP packet carrying the SRv6 SID of P1 and the End SID of PE2, encapsulates an SRH into the packet, and then forwards the packet. In this case, the value of the Hop Limit field in the IPv6 header is set to 1 and decrements by 1 each time the packet passes through a device. When the value of the Hop Limit field is 0, the packet is discarded, and then an ICMPv6 Time Exceeded message is sent to PE1.
  After receiving the UDP packet, P1 changes the value of the Hop Limit field to 0 and sends an ICMPv6 Time Exceeded message to PE1.
  After receiving the ICMPv6 Time Exceeded message from P1, PE1 increments the value of the Hop Limit field by 1 (the value now becomes 2) and continues to send the UDP packet.
  After receiving the UDP packet, P1 changes the value of the Hop Limit field to 1 and forwards the packet to PE2.
  After receiving the UDP packet, PE2 changes the value of the Hop Limit field to 0, determines that the SID type is End SID, and checks whether the upper-layer protocol header is a UDP or an ICMPv6 header.

## Slide 66: Overview of Tunnel Protection Technologies
SRv6 tunnel protection can be classified into local protection and E2E protection.
Local Protection
E2E protection
Ingress
Egress
Ingress
Egress
Fast switching
Only links and nodes protected
Detection-dependent fast switching
E2E paths protected
TI-LFA FRR
HSB
Midpoint TI-LFA FRR
Microloop avoidance
ECMP
Best-effort path

## Slide 67: TI-LFA FRR
TI-LFA FRR provides link and node protection for SRv6 tunnels. It enables traffic to be rapidly switched to the backup path if a link or node failure occurs.
As shown in the figure, the shortest path from PE1 to PE2 is PE1 -> P1 -> P4 -> PE2, which is the primary path. P1 needs to compute a TI-LFA backup path to PE2 through the following operations:
  Excludes the primary next hop (link P1 -> P4) and computes the post-convergence shortest path: P1 -> P2 -> P3 -> P4 -> PE2.
  Computes the P space and Q space, which are (P1, P2) and (P3, P4, PE2), respectively.
  Computes the TI-LFA backup path. In this case, any path can be represented as a multi-segment path (source node <-> P <-> Q <-> destination node). Both the segments from the source node to the P node and from the Q node to the destination node are loop-free. The P-to-Q path is expressed using a strict explicit path (End.X SID), ensuring that the entire TI-LFA strict explicit path is loop-free. To simplify repair path computation, P2 (which is farthest from the source node and resides in the P space), P3 (which is farthest from the destination node and resides in the Q space), and a link between the P and Q spaces are selected.
  After detecting that the P1-to-PE2 link goes down, P1 uses backup forwarding entries and encapsulates a new SRH into the packet, with the segment list being <FC03::C4, FC06::6>. In addition, the node changes the IPv6 destination address to FC03::C4 and then forwards the packet to the backup outbound interface in the B-to-C direction.
P1
PE1
PE2
Q space
P space
End.X FC03::C4
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
P2
P3
P4
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 0) FC03::C4
SRH (SL = 1) FC06::6 FC05::5
Payload
DIPv6: FC05::5 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC05::5
Payload
DIPv6: FC05::5 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC05::5
Payload
DIPv6: FC05::5 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC05::5
Payload
DIPv6: FC06::6 SIPv6: FC01::1
SRH (SL = 0) FC06::6 FC05::5
Payload
Local Protection Technology
E2E Protection Technology
Notes: P space and Q space:
  P space: is a set of nodes reachable from the source node of a protected link using the shortest path tree (SPT) rooted at the source node without traversing the protected link.
  Extended P space: is a set of nodes reachable from all the neighbors of a protected link's source node using SPTs rooted at the neighbors without traversing the protected link.
  Q space: is a set of nodes reachable from the destination node of a protected link using the reverse SPT rooted at the destination node without traversing the protected link.
Advantages of TI-LFA:
  Provides protection for all topologies, preventing cost planning from affecting protection path computation.
  Simplifies deployments. Backup paths are computed based on an IGP, eliminating the need to deploy additional protocols for reliability purposes.
  Preferentially uses the post-convergence path as the backup path, reducing the number of path switchovers and facilitating bandwidth planning.

## Slide 68
Notes: TI-LFA computation rules
  Priority: SRLG disjoint > Node protection > Link protection > Minimum cost
  TI-LFA computes a backup path that meets both the SRLG disjoint and node protection conditions. If multiple backup paths meet the two conditions, TI-LFA selects the path with the minimum cost.
  If no qualified backup path is available, TI-LFA computes a backup path that meets both the SRLG disjoint and link protection conditions. If multiple backup paths meet the two conditions, TI-LFA selects the path with the minimum cost.
  If no qualified backup path is available, TI-LFA computes a backup path that meets the node protection condition with the minimum cost.
  If no qualified backup path is available, TI-LFA computes a backup path that meets the link protection condition with the minimum cost.

## Slide 69: Limitations of TI-LFA FRR
In SRv6 Policy scenarios, the forwarding path of data packets usually needs to be constrained by specifying the nodes or links they need to traverse. However, if some nodes or links that must be traversed are faulty, TI-LFA FRR cannot provide protection.
PE1
P1
P2
P3
P4
PE2
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC03::3
Payload
Cost: 100
Cost: 10
Cost: 10
Cost: 10
Using TI-LFA, P1 computes the backup path to P3: P1 -> P2 -> P4 -> P3.
DIPv6: FC04::C4 SIPv6: FC0::1
SRH (SL = 1) FC03::3 FC04::C4
SRH (SL = 1) FC06::6 FC03::3
Payload
End.X FC04::C4
P2 fails, causing a data forwarding failure.
Backup path
Primary path
Local Protection Technology
E2E Protection Technology

## Slide 70: Overview of Midpoint Protection
In SRv6 Policy scenarios, strict node constraints may result in a TI-LFA FRR protection failure. To resolve this issue, a proxy forwarding node (a node upstream to the failed midpoint) takes over from the failed midpoint to complete the forwarding.
Specifically, after detecting that the next-hop interface of the packet fails, the next-hop address is the destination address of the packet, and the SL value is greater than 0, the proxy forwarding node performs the End behavior on behalf of the midpoint. The behavior involves decrementing the SL value by 1, copying the next SID to the DA field in the outer IPv6 header, and then forwarding the packet according to the instruction bound to the SID. In this way, the failed midpoint is bypassed, achieving SRv6 midpoint protection.
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC03::3
Payload
Proxy forwarding node
The backup path does not pass through P2.
Backup path
Primary path
PE1
P1
P2
P3
P4
PE2
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
Cost: 100
Cost: 10
Cost: 10
Cost: 10
Local Protection Technology
E2E Protection Technology

## Slide 71: Midpoint Protection Implementation
Midpoint protection is implemented as follows:
  Typically, P1 computes the shortest IGP path and TI-LFA backup path to each node, such as PE2.
  After midpoint TI-LFA is configured for P1 and P2 fails, P1 detects that the outbound interface of P2 is faulty. The destination address of the packet is P2, which is a neighbor directly connected to P1. In addition, the SL value in the SRH is greater than 0. In this case, the midpoint TI-LFA action is triggered.
  P1 performs proxy forwarding. Specifically, it decrements the SL value by 1, copies the next SID FC06::6 to the IPv6 destination address, and forwards the traffic to PE2 based on the destination address. In this way, the traffic can successfully reach PE2 through the P1 -> P3 -> P4 path.
  If P1 finds that the next hop to PE2 is still P2 after performing proxy forwarding, P1 forwards the traffic to the TI-LFA backup path. In other words, after implementing midpoint TI-LFA, P1 implements basic TI-LFA processing to enable the traffic to be switched to the correct backup path.
  After completing IGP convergence, PE1 deletes the FIB entries destined for P2. In this case, if iMaster NCE-IP delivers the segment list of a new policy, PE2 also performs proxy forwarding: decrementing the SL value by 1, using the next SID FC06::6 as the IPv6 destination address, and forwarding the traffic to PE2.
PE1
P1
P2
P3
P4
PE2
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
DIPv6: FC03::3 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC03::3
Payload
Backup path
Primary path
DIPv6: FC06::6 SIPv6: FC01::1
SRH (SL = 0) FC06::6 FC03::3
Payload
DIPv6: FC06::6 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC04::C4
SRH (SL = 0) FC06::6 FC03::3
Payload
DIPv6: FC06::6 SIPv6: FC01::1
SRH (SL = 0) FC06::6 FC03::3
Payload
TI-LFA is implemented again.
Local Protection Technology
E2E Protection Technology

## Slide 72: Microloop Introduction
TI-LFA FRR and midpoint protection can maintain data forwarding for a short time before IGP convergence is complete. After IGP convergence, however, data is forwarded through IGP routes instead of FRR (tunnel mode).
However, the convergence speed of devices on the live network may be different. As a result, a temporary loop, which is called a microloop, may be generated. The loop disappears only after all routers on the forwarding path complete convergence.
Primary path
FRR path
Post-convergence primary path
After IGP convergence, data is forwarded along the primary path.
DIPv6: C SIPv6: A
SRH (SL=1) D C
Payload
DIP: A SIP: B
Payload
DIP: A SIP: B
Payload
If the primary path fails, traffic is forwarded along the FRR path.
P1
PE1
PE2
P2
P3
P4
DIP: PE2 SIP: PE1
Payload
Cost: 1000
P1 completes IGP convergence and does not forward traffic based on FRR.
P2 does not complete IGP convergence and forwards data based on the original routing table.
P1 considers that the packet destined for PE2 should be sent to P2, but P2 considers that the packet destined for PE2 should be sent to P1.
Local Protection Technology
E2E Protection Technology

## Slide 73: Local Microloop in a Traffic Switchover Scenario
In a traffic switchover scenario, a local microloop occurs when a node adjacent to the failed node converges earlier than the other nodes on the network.
  When the link between P1 and P4 fails, traffic is first forwarded along the TI-LFA backup path.
  After P1 completes convergence, the next hop becomes P2, so that P1 forwards the traffic to P2 along the post-convergence path.
  Because P2 and other nodes on the network have not converged, the next hop for the traffic from P2 to PE2 is still P1. In this case, a loop is formed between P1 and P2 until P2 completes convergence.
P1
PE1
PE2
P2
P3
P4
DIP: PE2 SIP: PE1
Payload
Cost: 1000
P1 completes IGP convergence and does not forward traffic based on FRR.
P2 does not complete IGP convergence and forwards data based on the original routing table.
P1 considers that the packet destined for PE2 should be sent to P2, but P2 considers that the packet destined for PE2 should be sent to P1.
Local Protection Technology
E2E Protection Technology

## Slide 74: Local Microloop Avoidance in a Traffic Switchover Scenario
The microloop avoidance measure is to deliver the corresponding forwarding path after the involved node has already completed convergence for a period of time. This prevents the loop caused by IGP convergence on the node adjacent to the failed node. The detailed process is as follows:
  After P1 detects the fault of the link connected to P4, it enters the TI-LFA process and forwards the packet to PE2 along the TI-LFA backup path.
  P1 starts a timer. Before the timer expires, the forwarding table retains unchanged, and the TI-LFA backup path continues to be used for packet forwarding.
  When the timer expires, other nodes on the network have completed convergence. P1 can now perform convergence and then forward the packet along the post-convergence path.
Because each TI-LFA backup path is loop-free, the packet can be forwarded along a TI-LFA backup path for a period of time, and then the TI-LFA process can exit after the other nodes complete convergence.
P1
PE1
PE2
P2
P3
P4
DIPv6: FC06::6 SIPv6: FC01::1
Payload
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC03::C4
Payload
FC01::1
FC06::6
FC02::2
FC03::3
FC04::4
FC05::5
End.X FC03::C4
DIPv6: FC06::6 SIPv6: FC01::1
Payload
DIPv6: FC06::6 SIPv6: FC01::1
Payload
DIPv6: FC06::6 SIPv6: FC01::1
Payload
The P1 continues to forward traffic along the TI-LFA backup path before the timer expires.
Local Protection Technology
E2E Protection Technology

## Slide 75: Remote Microloop in a Traffic Switchover Scenario
If a remote fault occurs, a loop may also be formed between nodes.
A loop may occur if the node closer to the failure point converges earlier than the node farther from the failure point on the packet forwarding path.
  After detecting a fault on the P3 -> P4 link, a node (for example, P3) performs delayed convergence and forwards traffic along a TI-LFA backup path. In this case, only P3 performs delayed convergence, and the other nodes on the network still perform normal IGP convergence.
  P2 converges first and computes the P2 -> P1 -> P5 -> PE2 path as the new path to PE2. As such, after arriving at P2, the traffic is sent back to P1 instead of being forwarded to P3.
  Because P1 has not completed convergence, it still forwards the traffic along the P1 -> P2 -> P3 -> P4 -> P5 -> PE2 path. As a result, the traffic is sent back to P2, forming a loop.
P1
PE1
PE2
P2
P4
P5
DIP: PE2 SIP: PE1
Payload
P2 completes IGP convergence and forwards data based on the post-convergence routing table.
P1 does not complete IGP convergence and forwards data based on the original routing table.
P3
Cost: 1000
Local Protection Technology
E2E Protection Technology

## Slide 76: Remote Microloop Avoidance in a Traffic Switchover Scenario
A network node can pre-compute a loop-free backup path only when a directly connected link or node fails. That is, no loop-free path can be pre-computed against any other potential fault on the network. As such, a loop-free path needs to be computed after node convergence is completed, thereby resolving the microloop issue.
As shown in the following figures, the loop-free TI-LFA path P2 -> P1 -> P5 -> PE2 is computed after P2 converges. The loop-free path computed by P3 can be either a strict explicit one or a loose one.
P1
PE1
PE2
P2
P4
P5
P3
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
FC07::7
DIPv6: FC07::7 SIPv6: FC01::1
Payload
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 2) FC07::7 FC02::C4 FC03::C4
Payload
End.X FC03::C4
End.X FC02::C4
P1
PE1
PE2
P2
P4
P5
P3
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
FC07::7
DIPv6: FC07::7 SIPv6: FC01::1
Payload
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 1) FC07::7 FC02::C4
Payload
End.X FC02::C4
Strict explicit path
Loose path
Local Protection Technology
E2E Protection Technology

## Slide 77: Microloop in a Traffic Switchback Scenario
Due to the lack of a convergence order in distributed computing, a microloop may occur in a traffic switchback scenario.
  Assume that the link between P1 and P4 fails, and the path from PE1 to PE2 is PE1 -> P1 -> P2 -> P3 -> P4 -> PE2.
  If the link between P1 and P4 recovers and P2 completes convergence, the path from P2 to PE2 is P2 -> P1 -> P4 -> PE2. In this case, P2 forwards traffic to P1.
  If P1 has not completed IGP convergence due to some reasons, for example, a large number of services are running or CPU usage is high, the node still forwards the traffic back to P2 through the original path, forming a loop.
P1
PE1
PE2
P2
P3
P4
Cost: 1000
The faulty link recovers.
P2 completes convergence and considers that the traffic destined for PE2 should be sent to P1.
P1 does not complete convergence and considers that the traffic destined for PE2 should be sent to P2.
DIP: PE2 SIP: PE1
Payload
A loop is formed between P1 and P2.
Local Protection Technology
E2E Protection Technology

## Slide 78: Microloop Avoidance in a Traffic Switchback Scenario
The method of microloop avoidance in a traffic switchback scenario is similar to that of remote microloop avoidance in a traffic switchover scenario.
As shown in the following figures, after P2 completes convergence, it encapsulates a new SRH into the packet, enabling traffic to be forwarded along the post-convergence path (which is a strict explicit path) to the destination address. After P1 converges, it forwards the traffic to PE2 along the post-convergence path.
P1
PE1
PE2
P3
P4
P2
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
DIPv6: FC06::6 SIPv6: FC01::1
Payload
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 2) FC06::6 FC02::C4 FC03::C4
Payload
End.X FC03::C4
End.X FC02::C4
Strict explicit path
P1
PE1
PE2
P3
P4
P2
FC01::1
FC02::2
FC03::3
FC04::4
FC05::5
FC06::6
DIPv6: FC06::6 SIPv6: FC01::1
Payload
DIPv6: FC03::C4 SIPv6: FC01::1
SRH (SL = 1) FC06::6 FC02::C4
Payload
End.X FC02::C4
Loose path
The faulty link recovers.
The faulty link recovers.
Local Protection Technology
E2E Protection Technology

## Slide 79: SRv6 Policy HSB
E2E SRv6 Policy protection can be implemented by configuring two candidate paths with different preferences for an SRv6 Policy. The path with a higher preference is the primary and that with a lower preference is the backup. SBFD is enabled for the two paths.
When SBFD on the primary path detects a fault, traffic is switched from the primary path to the backup path.
If some devices on an SRv6 network do not support SRv6, local protection cannot be implemented. In this case, HSB can be used to provide high reliability.
CE1
PE1
PE2
P1
P2
P3
P4
PE3
PE4
CE2
Primary path
Backup path
SRv6-incapable
SRv6 policy PE1toPE3
endpoint PE3 color 100
candidate-path preference 200 //Primary
segment-list <PE1.End, PE3.End>
candidate-path preference 100 //Backup
segment-list <PE2.End, P2.End, PE4.End, PE3.End >
Local Protection Technology
E2E Protection Technology

## Slide 80: SRv6 Policy ECMP
During SRv6 Policy deployment, two segment lists can be configured in a candidate path to implement SRv6 Policy load balancing. In this way, data is load balanced between two paths.
If one of the paths fails, data can still be forwarded over the other path.
CE1
PE1
PE2
P1
P2
P3
P4
PE3
PE4
CE2
ECMP path
SRv6 policy PE1toPE3
endpoint PE3 color 100
candidate-path preference 200
segment-list <PE1.End, PE3.End> //ECMP
segment-list <PE2.End, P2.End, PE4.End , PE3.End > //ECMP
Local Protection Technology
E2E Protection Technology

## Slide 81: Best-Effort Paths for SRv6 Policies
If SBFD on PE1 detects that both the primary and backup paths fail, PE1 forwards traffic over an SRv6 BE tunnel.
CE1
PE1
PE2
P1
P2
P3
P4
PE3
PE4
CE2
Primary path
Backup path
The primary path fails.
The backup path fails.
Best-effort path
Traffic is carried over SRv6 BE.
BGP 100
ipv6-family vpn-instance vpn1
segment-routing ipv6 traffic-engineer best-effort
Local Protection Technology
E2E Protection Technology

## Slide 82
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
  Overview of SRv6 High Reliability
  SRv6 Tunnel Status Detection and Tunnel Protection
  SRv6 Egress Protection and Access Protection
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 83: Overview of SRv6 Egress Protection
The tunnels of an SRv6 Policy have the same headend. In this case, the specific tunnel is determined using <Color, Endpoint>. If the endpoint of the tunnel fails, data cannot be sent to the destination network segment.
As such, local protection and E2E protection technologies commonly used for SRv6 tunnels can protect only the source PE and transit nodes (Ps), but not the SRv6 endpoint.
If a fault occurs on the endpoint, it is mainly rectified through VPN FRR. In addition, it can also be rectified through anycast FRR or mirror protection.
CE1
PE1
PE2
P1
P2
P3
P4
PE3
PE4
CE2
Local protection path
E2E protection path
A fault on a transit link or node can be rectified through both local protection and E2E protection.
Primary path
Local protection path
E2E protection path
A fault on the endpoint cannot be rectified through local protection or E2E protection.
Notes: Anycast FRR and mirror protection technologies are complex and therefore rarely used on live networks.

## Slide 84: VPN FRR
VPN FRR helps rectify endpoint faults by directly forming VPN backup routes. It is implemented as follows:
  The source PE pre-computes primary and backup routes based on the two learned VPN routes with different next-hop PEs and then delivers the computed routes to the FIB table. In addition, after detecting a remote PE fault through BFD, the source PE switches VPN traffic to the backup path before VPN route convergence.
CE1
PE1
P1
P2
PE3
CE2
PE2
BGP Route
Prefix NHP
Net2 PE2
Net2
BGP Route
Prefix NHP
Net2 PE3
PE1's BGP Route
Prefix NHP
Net2 PE2
Backup PE3
Primary path
Backup path

## Slide 85: Anycast FRR
Anycast FRR implements SRv6 egress protection by deploying the same locator and VPN SID on the PEs to which a CE is dual-homed.
CE1
PE1
PE2
P1
P2
PE3
PE4
CE2
Primary path
Local protection path
P1 where TI-LFA is deployed pre-computes a backup path to FC05:: /96.
FC05:: /96
FC05:: /96
End.DT4
FC05::100
End.DT4
FC05::100
DIPv6: FC05::100 SIPv6: FC01::1
Payload
End.X
FC04::C4
Payload: CE1 -> CE2
FC01:: /96
DIPv6: FC04::C4 SIPv6: FC01::1
SRH (SL = 1) FC05::100 FC04::C4
Payload
Payload: CE1 -> CE2
Notes: Anycast FRR can be used in both egress protection and local protection scenarios.
Although anycast FRR can provide protection against PE failures, it has the following drawbacks:
  VPN SIDs must be manually configured to ensure that the two PEs configured with the same VPN instance have the same VPN SID.
  Only IGP route selection (not VPN route selection) can be performed. For example, if VPN services need to be load-balanced between PE3 and PE4 or the route advertised by PE3 needs to be preferentially selected, VPN route selection cannot be performed if the route advertised by PE4 is preferentially selected through an IGP on the path to FC05::.
  If there is a PE-CE link interface failure, such as a failure on the link between PE3 and CE2, traffic is still forwarded to PE3 and then to PE4, resulting in a traffic loop that cannot be eliminated.

## Slide 86: SRv6 Access Protection
When a CE is dual-homed to PEs, if the link between the CE and endpoint PE fails, traffic may be lost. In this case, mixed FRR can be used to resolve this problem.
PE2 receives a VPN route from CE2 and another VPN route from PE3, forming FRR protection. When the link between PE2 and CE2 fails, PE2 detects the fault and steers all relevant traffic to the backup path to PE3. In this case, the next hop of the primary path is an access interface and the backup path is an SRv6 tunnel, forming mixed FRR protection.
CE1
PE1
P1
P2
PE3
CE2
PE2
Net2
PE3 advertises a VPN route to PE2.
CE2 advertises common routes to PE2 and PE3.
PE2's BGP Route
Prefix NHP Out-Int
Net2 CE2 PE2 -> CE2 link interface
Backup PE3 SRv6 Tunnel
When the path from PE2 to CE2 fails, the forwarding path becomes PE2 -> PE3 -> CE2.
Primary path
Backup path

## Slide 87
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
Basic SRv6 Configuration
  SRv6 BE
  SRv6 Policy
SRv6 Deployment Using iMaster NCE-IP

## Slide 88: L3VPNv4 over SRv6 BE (1)
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SRv6 BE paths on the backbone network to enable CE1 and CE2 to communicate through Loopback1.
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Notes: The experiment configuration is based on the NE20E-S2F (software version: NE20E V800R012C10SPC300). The configuration roadmaps for different devices are similar. For details, see the corresponding product documentation.

## Slide 89: L3VPNv4 over SRv6 BE (2)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Establish an MP-IBGP peer relationship between the PEs. The configuration on PE1 is used as an example.
[~PE1] bgp 100
[~PE1-bgp] peer 2001:DB8:3::3 as-number 100
[*PE1-bgp] peer 2001:DB8:3::3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
Check the VPNv4 peer relationship on PE1.
<PE1>display bgp vpnv4 all peer
BGP local router ID : 10.0.1.1
Local AS number : 100
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent Up/Down State
2001:DB8:3::3 4 100 3 4 00:00:04 Established

## Slide 90: L3VPNv4 over SRv6 BE (3)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
Establish an SRv6 BE path between the PEs. PE1 configurations are as follows: (PE2 configurations are not provided here, and the P does not require such configurations.)
[~PE1] segment-routing ipv6
[*PE1-segment-routing-ipv6] encapsulation source-address 2001:DB8:1::1
[*PE1-segment-routing-ipv6] locator as100 ipv6-prefix 2001:DB8:100:: 64 static 32
[*PE1-segment-routing-ipv6-locator] quit
[*PE1-segment-routing-ipv6] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 prefix-sid
[*PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
[~PE1] isis 1
[~PE1-isis-1] segment-routing ipv6 locator as100
[*PE1-isis-1] commit
[~PE1-isis-1] quit
Notes: Configure basic SRv6 functions as follows:
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the encapsulation source-address ipv6-address [ ip-ttl ttl-value ] command to configure a source address for SRv6 VPN encapsulation.
    When traffic enters an SRv6 VPN tunnel, the address configured using this command functions as the source address in the IPv6 header. The source address must be an existing interface address on the device.
  Run the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command to configure an SRv6 locator.
    The Locator field corresponds to the ipv6-prefix ipv6-address parameter and its length is determined by the prefix-length parameter. A locator identifies an IPv6 subnet on which all IPv6 addresses can be allocated as SRv6 SIDs. After a locator is configured for a node, the system generates a locator route through which other nodes can locate this node. In addition, all SIDs advertised by the node are reachable through the route.
    The Function field is also called opcode, which can be dynamically allocated using an IGP or be configured using the opcode command. When configuring a locator, you can use the static static-length parameter to specify the static segment length, which determines the number of static opcodes that can be configured in the locator. In dynamic opcode allocation, the IGP allocates opcodes outside the range of the static segment, so that no SRv6 SID conflict occurs.

## Slide 91
Notes:   (Optional) Run the opcode func-opcode end-dt4 vpn-instance vpn-instance-name command to configure a static SID opcode.
    An End.DT4 SID can be dynamically allocated by BGP or be manually configured. If you want to use the segment-routing ipv6 locator locator-name command to enable dynamic End.DT4 SID allocation by BGP in the future, skip this step.
  Run the quit command to exit the SRv6 locator view.
  Run the quit command to exit the SRv6 view.
Enable IS-IS SRv6.
  Run the isis [ process-id ] command to enter the IS-IS view.
  Run the ipv6 enable topology ipv6 command to enable the IPv6 capability for the IS-IS process in the IPv6 topology.
  Run the segment-routing ipv6 locator locator-name [ auto-sid-disable ] command to enable IS-IS SRv6.
    segment-routing ipv6 locator locator-name: enables IS-IS SRv6 and dynamic SID allocation. SIDs must be allocated within the locator range.
    segment-routing ipv6 locator locator-name auto-sid-disable: enables IS-IS SRv6 and disables dynamic SID allocation so that SIDs are statically allocated within the locator range.
    During SRv6 SID allocation, if a static opcode is configured, the static opcode is preferentially used to form a static SID. If no static opcode is configured, a SID is dynamically allocated. The process of dynamic SRv6 SID allocation using IS-IS is as follows:
    Configure a locator in the SRv6 view, and run the segment-routing ipv6 locator command in the IS-IS process view to enable SRv6 and reference the locator. An IS-IS process can reference multiple locators. However, only one locator can be used to advertise End/End.X SIDs.
    IS-IS allocates an End SID to each locator in the range of the dynamic segment based on locator configurations. Both PSP and non-PSP SIDs can be allocated.
    Configure IPv6 addresses for interfaces and enable IS-IS IPv6. IS-IS allocates both PSP and non-PSP End.X SIDs to the interfaces in the range of the dynamic segment based on locator configurations.
  Run the quit command to exit the IS-IS view.
Configure the device to add SIDs to VPN routes.
  Run the peer ipv6-address prefix-sid command to enable the device to exchange IPv4 prefix SID information with the specified IPv6 peer.

## Slide 92: L3VPNv4 over SRv6 BE (4)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
Enable the VPN instance IPv4 address family on each PE. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[~PE1] bgp 100
[*PE1-bgp] ipv4-family vpn-instance vpna
[*PE1-bgp-vpna] peer 10.0.14.4 as-number 65000
[*PE1-bgp-vpna] segment-routing ipv6 best-effort
[*PE1-bgp-vpna] segment-routing ipv6 locator as100
[*PE1-bgp-vpna] commit
[~PE1-bgp-vpna] quit
[~PE1-bgp] quit
Notes: Configure VPN routes to recurse to SRv6 BE paths based on the carried SIDs.
  Run the bgp { as-number-plain | as-number-dot } command to enter the BGP view.
  Run the ipv4-family vpn-instance vpn-instance-name command to enter the BGP-VPN instance IPv4 address family view.
  Run the segment-routing ipv6 best-effort command to enable VPN route recursion based on the SIDs carried by routes.
  Run the segment-routing ipv6 locator locator-name [ auto-sid-disable ] command to enable the device to add SIDs to VPN routes.
  If auto-sid-disable is not specified, dynamic SID allocation is supported. If there are static SIDs in the range of the locator specified using locator-name, the static SIDs are used. Otherwise, dynamically allocated SIDs are used. If auto-sid-disable is specified, BGP does not dynamically allocate SIDs.
  Run the commit command to commit the configuration.

## Slide 93: L3VPNv4 over SRv6 BE (5)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Check the local SID table containing all types of SRv6 SIDs on PE2.
<PE2>display segment-routing ipv6 local-sid forwarding
My Local-SID Forwarding Table
-------------------------------------
SID : 2001:DB8:300::1:0:0/128 FuncType : End
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:1/128 FuncType : End
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:2/128 FuncType : End.X
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:3/128 FuncType : End.X
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:20/128 FuncType : End.DT4
LocatorName: as100
PE2 locally generates an End.DT4 SID and advertises the SID to PE1.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.

## Slide 94: L3VPNv4 over SRv6 BE (6)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Check VPNv4 routing information on PE1.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
<PE1>display bgp vpnv4 al routing-table 10.1.5.5
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 10.1.5.5/32:
Label information (Received/Applied): 3/NULL
From: 2001:DB8:3::3 (10.0.3.3)
Route Duration: 0d00h15m54s
Relay IP Nexthop: FE80::DE99:14FF:FE7A:C301
Relay IP Out-Interface: GigabitEthernet0/3/0.12
Relay Tunnel Out-Interface:
Original nexthop: 2001:DB8:3::3
Qos information : 0x0
Ext-Community: RT <111 : 1>
Prefix-sid: 2001:DB8:300::1:0:20
AS-path Nil, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 20
Not advertised to any peer yet
IPv6 address of the peer; SID corresponding to 10.1.5.5 (the same as that locally allocated on PE2)

## Slide 95: L3VPNv4 over SRv6 BE (7)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
<PE1> display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Route Flags: R - relay, D - download to fib, T - to vpn-instance, B - black hole route
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 2001:DB8:300::1:0:20 Neighbour: 2001:DB8:3::3
State: Active Adv Relied Age: 00h17m40s
Tag: 0 Priority: low
Label: 3 QoSInfo: 0x0
IndirectID: 0x1000177 Instance:
RelayNextHop: 2001:DB8:300::1:0:20 Interface: SRv6 BE
TunnelID: 0x0 Flags: RD
Check vpna's routing information on PE1.
PE1 uses this IPv6 address as the next-hop address to forward packets destined for 10.1.5.5.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.
Interface type: SRv6 BE

## Slide 96: L3VPNv4 over SRv6 BE (8)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Verify the configuration.

## Slide 97
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
Basic SRv6 Configuration
  SRv6 BE
  SRv6 Policy
SRv6 Deployment Using iMaster NCE-IP

## Slide 98: L3VPNv4 over SRv6 Policy (1)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SRv6 Policies on the backbone network to enable CE1 and CE2 to communicate through Loopback1.
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.

## Slide 99: L3VPNv4 over SRv6 Policy (2)
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Establish an MP-IBGP peer relationship between the PEs.
[~PE1] bgp 100
[~PE1-bgp] peer 2001:DB8:3::3 as-number 100
[*PE1-bgp] peer 2001:DB8:3::3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
Check the VPNv4 peer relationship on PE1.
<PE1>display bgp vpnv4 all peer
BGP local router ID : 10.0.1.1
Local AS number : 100
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent Up/Down State
2001:DB8:3::3 4 100 3 4 00:00:04 Established
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
Notes: The SIDs of PE1, the P, and PE2 are 2001:DB8:1000::111, 2001:DB8:2000::222, and 2001:DB8:3000::333, respectively.
In this experiment, the SRv6 Policy is established based on specified End SIDs.

## Slide 100: L3VPNv4 over SRv6 Policy (3)
Configure an SRv6 SID. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
[~PE1] segment-routing ipv6
[*PE1-segment-routing-ipv6] encapsulation source-address 2001:DB8:1::1
[*PE1-segment-routing-ipv6] locator as1000 ipv6-prefix 2001:DB8:1000:: 64 static 32
[*PE1-segment-routing-ipv6-locator] opcode ::111 end
[*PE1-segment-routing-ipv6-locator] quit
[*PE1-segment-routing-ipv6] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 prefix-sid
[*PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
[~PE1] isis 1
[~PE1-isis-1] segment-routing ipv6 locator as1000 auto-sid-disable
[*PE1-isis-1] commit
[~PE1-isis-1] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Manually configure an SRv6 End SID.
Notes: SRv6 paths are established using SIDs. Static SRv6 SIDs are recommended. The configuration procedure is as follows:
  Run the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command to configure an SRv6 locator.
  Run the opcode func-opcode end command to configure a static End SID opcode.
  Run the opcode func-opcode end-x interface interface-name nexthop nexthop-address [ no-psp ] command to configure a static End.X SID opcode.
  Run the quit command to exit the SRv6 locator view.

## Slide 101: L3VPNv4 over SRv6 Policy (4)
Configure an SRv6 Policy. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] segment-routing ipv6
[~PE1-segment-routing-ipv6] segment-list list1
[*PE1-segment-routing-ipv6-segment-list-list1] index 5 sid ipv6 2001:DB8:2000::222
[*PE1-segment-routing-ipv6-segment-list-list1] index 10 sid ipv6 2001:DB8:3000::333
[*PE1-segment-routing-ipv6-segment-list-list1] commit
[~PE1-segment-routing-ipv6-segment-list-list1] quit
[~PE1-segment-routing-ipv6] srv6-te-policy locator as1000
[*PE1-segment-routing-ipv6] srv6-te policy policy1 endpoint 2001:DB8:3::3 color 101
[*PE1-segment-routing-ipv6-policy-policy1] binding-sid 2001:DB8:1000::100
[*PE1-segment-routing-ipv6-policy-policy1] candidate-path preference 100
[*PE1-segment-routing-ipv6-policy-policy1-path] segment-list list1
[*PE1-segment-routing-ipv6-policy-policy1-path] commit
[~PE1-segment-routing-ipv6-policy-policy1-path] quit
[~PE1-segment-routing-ipv6-policy-policy1] quit
[~PE1-segment-routing-ipv6] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Specify SRv6 End SIDs for the P and PE2 in sequence.
Specify the color and endpoint.
Notes: Configure a segment list.
  Run the system-view command to enter the system view.
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the segment-list list-name command to configure a segment list (an explicit path) for an SRv6 Policy candidate path and enter the segment list view.
  Run the index index sid ipv6 ipv6address command to specify a next-hop SID for the segment list.
    You can run the command multiple times. The system generates a SID stack for the segment list by index index in ascending order. If a candidate path in the SRv6 Policy is preferentially selected, traffic is forwarded using the segment lists of the candidate path. A maximum of 10 SIDs can be configured for each segment list.
  Run the commit command to commit the configuration.

## Slide 102
Notes: Configure an SRv6 Policy.
  Run the system-view command to enter the system view.
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the srv6-te-policy locator locator-name command to associate a locator with the SRv6 Policy to be created. This configuration allows you to specify a binding SID for the SRv6 Policy in the locator range.
  Run the srv6-te policy name-value endpoint endpoint-ip color color-value command to create an SRv6 Policy and enter the SRv6 Policy view.
  (Optional) Run the binding-sid binding-sid command to configure a binding SID for the SRv6 Policy.
    The value of binding-sid must be within the range of the static segment specified using the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command.
  Run the candidate-path preference preference command to configure a candidate path and its preference for the SRv6 Policy.
    Each SRv6 Policy supports multiple candidate paths. A larger preference value indicates a higher candidate path preference. If multiple candidate paths are configured, the one with the highest preference takes effect.
  Run the segment-list list-name [ weight weight-value | path-mtu mtu-value ] * command to configure a segment list for the candidate path of the SRv6 Policy.
    The segment list must have been created using the segment-list (SRv6 view) command.
  Run the commit command to commit the configuration.

## Slide 103: L3VPNv4 over SRv6 Policy (5)
Enable the VPN instance IPv4 address family on each PE. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1-bgp] ipv4-family vpn-instance vpna
[*PE1-bgp-vpna] segment-routing ipv6 traffic-engineer best-effort
[*PE1-bgp-vpna] segment-routing ipv6 locator as1000
[*PE1-bgp-vpna] commit
[~PE1-bgp-vpna] quit
[~PE1-bgp] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Notes: segment-routing ipv6 traffic-engineer best-effort //If an SRv6 BE path exists on the network, you can set the best-effort parameter, allowing the SRv6 BE path to function as a best-effort path in the case of an SRv6 Policy fault.

## Slide 104: L3VPNv4 over SRv6 Policy (6)
Configure a tunnel policy and import VPN traffic. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] route-policy p1 permit node 10
[*PE1-route-policy] apply extcommunity color 0:101
[*PE1-route-policy] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 route-policy p1 import
[*PE1-bgp-af-vpnv4] quit
[*PE1-bgp] quit
[*PE1] tunnel-policy p1
[*PE1-tunnel-policy-p1] tunnel select-seq ipv6 srv6-te-policy load-balance-number 1
[*PE1-tunnel-policy-p1] quit
[*PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] tnl-policy p1
[*PE1-vpn-instance-vpna-af-ipv4] commit
[~PE1-vpn-instance-vpna-af-ipv4] quit
[~PE1-vpn-instance-vpna] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 105: L3VPNv4 over SRv6 Policy (7)
Check SRv6 Policy information on PE1.
<PE1>display srv6-te policy
PolicyName : policy1
Color : 101 Endpoint : 2001:DB8:3::3
TunnelId : 1 Binding SID : 2001:DB8:1000::100
TunnelType : SRv6-TE Policy DelayTimerRemain :
Policy State : Up
Admin State : UP Traffic Statistics : Disable
Candidate-path Count : 1
Candidate-path Preference : 100
Path State : Active Path Type : Primary
Protocol-Origin : Configuration(30) Originator : 0, 0.0.0.0
Discriminator : 100 Binding SID : 2001:DB8:1000::100
GroupId : 1 Policy Name : policy1
DelayTimerRemain : - Segment-List Count : 1
Segment-List : list1
Segment-List ID : 1 XcIndex : 1
List State : Up DelayTimerRemain : -
Weight : 1 BFD State : -
SID :
2001:DB8:2000::222
2001:DB8:3000::333
Color of the specified SRv6 Policy
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 106: L3VPNv4 over SRv6 Policy (8)
Check VPNv4 routing information on PE1.
<PE1> display bgp vpnv4 all routing-table 10.1.5.5
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 10.1.5.5/32:
Label information (Received/Applied): 3/NULL
From: 2001:DB8:3::3 (10.0.13.3)
Route Duration: 0d00h03m30s
Relay IP Nexthop: FE80::DE99:14FF:FE7A:C301
Relay IP Out-Interface: GigabitEthernet0/3/0.12
Relay Tunnel Out-Interface:
Original nexthop: 2001:DB8:3::3
Qos information : 0x0
Ext-Community: RT <111 : 1>, Color <0 : 101>
Prefix-sid: 2001:DB8:3000::1:0:1E
AS-path 65000, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 20
Not advertised to any peer yet
The route recurses to the corresponding SRv6 Policy based on the color attribute.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 107: L3VPNv4 over SRv6 Policy (9)
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
Check vpna's routing information on PE1.
<PE1>display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 2001:DB8:3::3 Neighbour: 2001:DB8:3::3
State: Active Adv Relied Age: 00h08m38s
Tag: 0 Priority: low
Label: 3 QoSInfo: 0x0
IndirectID: 0x1000174 Instance:
RelayNextHop: :: Interface: policy1
TunnelID: 0x000000003400000001 Flags: RD
The outbound interface is an SRv6 Policy interface.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs for them to exchange routing information.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 108
SRv6 Overview
SRv6 Fundamentals
SRv6 High Reliability
Basic SRv6 Configuration
SRv6 Deployment Using iMaster NCE-IP

## Slide 109: SRv6 Deployment Using iMaster NCE-IP
Static SRv6 deployment on the live network poses great challenges to network O&M. For example, static SRv6 deployment takes a long period and does not support global path planning or network quality-based SRv6 forwarding path adjustment.
Deploying SRv6 through iMaster NCE-IP can avoid the problems faced by static SRv6 deployment.
iMaster NCE-IP uses the following protocols to deploy SRv6 tunnels and VPN services:
  BGP-LS
  BGP IPv6 SR Policy
  NETCONF
R2
R3
iMaster NCE-IP
R1
IGP
R4
SRv6 Policy
NETCONF/BGP-LS/BGP SR Policy
Notes: IGP: generates network topology information, such as bandwidth, delay, and SID information, on a router.
BGP-LS: collects topology information and reports collected information to the controller. If an RR exists on the network, you only need to deploy BGP-LS on the RR and establish a BGP-LS peer relationship between the RR and controller.
BGP IPv6 SR Policy: Such a peer relationship is established between the controller and forwarder, so that the controller can deliver an SRv6 Policy to the forwarder through the peer relationship to direct traffic forwarding. To reduce the number of peer relationships, you can deploy an RR and configure PEs and the controller to function as RR clients.
NETCONF: delivers service configurations from the controller to forwarders. This document does not describe service delivery or NETCONF-related configuration.

## Slide 110: SRv6 Policy Advertisement Process
To facilitate configuration, the controller provides the following functions:
  Directly creates a bidirectional tunnel between the ingress and egress. In other words, a tunnel from the egress to the ingress is automatically created when a tunnel from the ingress to the egress is created.
  Allows you to configure tunnel and color templates to simplify the configuration of some parameters.
In Huawei's CloudWAN solution:
  The SRv6 Policy configurations are delivered by BGP IPv6 SR Policy, and the tunnel status is reported by BGP-LS.
RR
PE1
PE2
P1
PE4
PE3
BGP-LS
BGP IPv6 SR-Policy
Network administrator
2
Requirement input
Automatic path planning by the controller
3
Network topology reporting
1
Forwarding path deployment
4
SRv6 Policy
BGP-LS peer
BGP SR-Policy peer
Tunnel status reporting
5
Notes: The process of planning and deploying forwarding paths through iMaster NCE-IP is as follows:
  Devices use BGP-LS to report network topology information to the controller, which then generates forwarding paths based on requirements.
  The controller delivers the computed paths to the devices through BGP IPv6 SR Policy.
  Target traffic travels along the delivered paths.

## Slide 111: Key Information Required for SRv6 Policy Path Computation
iMaster NCE-IP uses an IGP to collect the following key information for SRv6 Policy path computation:
  SID information: End and End.X SIDs.
  Locator information: After a locator is configured for a node, the system generates a locator route and propagates the route throughout the SR domain using an IGP. Other nodes on the network can locate this node through the locator route.
  Interface bandwidth information: physical bandwidth and reservable bandwidth.
  Interface delay and packet loss rate.
  Network topology information.
BGP-LS advertises the information collected by an IGP to iMaster NCE-IP.
R3
iMaster NCE-IP
R1
R2
BGP-LS
BGP-LS
BGP-LS
IGP
IGP
IGP

## Slide 112: Basic IGP Configurations
In Huawei's SRv6 solution, it is recommended that extended IS-IS be used as an IGP for the collection of basic network information.
Basic IGP configurations are as follows:
  Global IS-IS configurations
  Interface-specific IS-IS configurations
[P1]isis 1
[P1-isis-1] is-level level-2
[P1-isis-1] cost-style wide //TE information (such as bandwidth information) required in TE scenarios cannot be carried in narrow mode. Therefore, the wide type needs to be set.
[P1-isis-1] network-entity 49.0001.0010.0000.0005.00
[P1-isis-1] is-name P1
[P1-isis-1] ipv6 enable topology ipv6
[P1-isis-1] ipv6 bgp-ls enable level-2 //The device is enabled to send topology information collected by IS-IS to the controller through BGP-LS. This function only needs to be configured on the RR. That is, only one device in the IGP domain needs to send topology information to the controller through BGP-LS.
[P1-isis-1] ipv6 advertise link attributes //The device is enabled to carry link attribute-related TLVs in LSPs. TLV information includes the IPv6 addresses and indexes of interfaces.
[P1-isis-1] ipv6 metric-delay advertisement enable level-1-2 //The device is enabled to advertise IPv6 delay information. Intra-domain IPv4 link delay information is collected and flooded through IS-IS and then reported to the controller through BGP-LS. Based on the delay information, the controller computes the optimal path on the P2P network.
[P1-isis-1] ipv6 traffic-eng level-2 //IS-IS TE is enabled so that link bandwidth information is reported to the TE module.
[P1]interface GigabitEthernet0/3/0
[P1-GigabitEthernet0/3/0] isis ipv6 enable 1
[P1-GigabitEthernet0/3/0] isis circuit-type p2p //The IS-IS interface's network type must be set to P2P. Otherwise, the required network topology cannot be formed on the controller.

## Slide 113: Topology Information Reporting to the Controller Through BGP-LS
Each router maintains one or more LSDBs. Each LSDB contains multiple link attributes, such as the interface IP address, link metric, TE metric, link bandwidth, and reservable bandwidth. The BGP process of a router obtains information from these LSDBs and carries the information in the extended NLRI attribute.
R2's LSDB
R1's link state information
R2's link state information
R3's link state information
R2's BGP process
R1's link state information
R2's link state information
R3's link state information
Extraction
Node NLRI
NLRI
Link NLRI
Topology Prefix NLRI
(IPv4)
Topology Prefix NLRI
(IPv6)
Reporting
Controller
Advertised to the BGP-LS peer

## Slide 114: BGP-LS Deployment
BGP-LS is mainly used to upload network topology and tunnel information. As such, iMaster NCE-IP needs to establish BGP-LS peer relationships with at least two types of devices:
  Establishes a BGP-LS peer relationship with an intra-AS network node, which is usually a BGP RR, in order to obtain network topology information.
  Establishes a BGP-LS peer relationship with the ingress of the involved tunnel in order to obtain SRv6 Policy status.
BGP-LS deployment solutions:
BGP-LS
PE1
P1
PE2
CE1
CE2
BGP-LS
PE1
RR
PE2
CE1
CE2
iMaster NCE-IP
iMaster NCE-IP
Solution 1: Establish BGP-LS peer relationships between iMaster NCE-IP and all PEs and between iMaster NCE-IP and all Ps.
Solution 2: Establish BGP-LS peer relationships between iMaster NCE-IP and RRs and between the RRs and other devices.
Solution 2 is recommended to reduce the number of BGP peers maintained by iMaster NCE-IP.

## Slide 115: BGP-LS Peer Relationship Establishment
[P1]bgp 65001
[P1-bgp]peer 2000::102 as-number 65001
[P1-bgp]peer 2000::102 connect-interface LoopBack0
[P1-bgp]link-state-family unicast
[P1-bgp-af-ls]peer 2000::102 enable
BGP-LS
[P1]display bgp link-state unicast peer
BGP local router ID : 1.0.0.5
Local AS number : 65001
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
2000::102 4 65001 72877 72106 0 1039h31m Established 0
2000::102
FC01::5
Notes: BGP-LS peer relationships can be established using IPv4 or IPv6 addresses. This course uses IPv6 addresses to establish such relationships.

## Slide 116: SRv6 Policy Path Computation and Deployment
With the SRv6 Policy path computation algorithm, the controller can provide the following path computation results if specified constraints are met:
  Minimum cost: path with the minimum cost among all qualified paths
  Minimum delay: path with the minimum delay among all qualified paths
  Bandwidth balancing: path with the most remaining bandwidth among all qualified paths that have the same cost
During SRv6 Policy creation, you need to specify a color value for each SRv6 Policy.
Notes: Optional constraints:
  Bandwidth constraint: ensures that the bandwidth configured for a service does not exceed the remaining bandwidth of the link that the service traverses.
  PIR constraint: ensures that the peak bandwidth does not exceed the BC0 bandwidth of the link that the service traverses. PIR refers to the peak bandwidth of a service.
  Delay limit constraint: ensures that the path delay of a service does not exceed the configured delay limit.
  Hop limit constraint: ensures that the number of links that a service traverses does not exceed the configured hop limit.
  Affinity constraint: determines which types of links are allowed and which types of links are not allowed for services.

## Slide 117: BGP IPv6 SR Policy Deployment
BGP IPv6 SR Policy is mainly used to deliver SRv6 tunnel information. As such, iMaster NCE-IP needs to establish a BGP IPv6 SR Policy peer relationship with the ingress of the involved tunnel.
BGP IPv6 SR Policy deployment solutions:
BGP IPv6 SR Policy
PE1
P1
PE2
CE1
CE2
BGP IPv6 SR Policy
PE1
RR
PE2
CE1
CE2
iMaster NCE-IP
iMaster NCE-IP
Solution 1: Establish BGP IPv6 SR Policy peer relationships between iMaster NCE-IP and all PEs.
Solution 2: Establish BGP IPv6 SR Policy peer relationships between iMaster NCE-IP and RRs and between the RRs and other devices.
Solution 2 is recommended to reduce the number of BGP peers maintained by iMaster NCE-IP.

## Slide 118: BGP IPv6 SR Policy Peer Relationship Establishment
[P1]bgp 65001
[P1-bgp]peer 2000::102 as-number 65001
[P1-bgp]peer 2000::102 connect-interface LoopBack0
[P1-bgp]ipv6-family sr-policy
[P1-bgp-af-ls]peer 2000::102 enable
BGP IPv6 SR Policy
[P1]display bgp sr-policy ipv6 peer
BGP local router ID : 1.0.0.5
Local AS number : 65001
Total number of peers : 7 Peers in established state : 5
Peer V AS MsgRcvd MsgSent OutQ Up/Down State PrefRcv
2000::102 4 65001 11286 11195 0 0160h44m Established 2
2000::102
FC01::5
Notes: BGP IPv6 SR Policy peer relationships can be established using IPv4 or IPv6 addresses. This course uses IPv6 addresses to establish such relationships.

## Slide 119: VPN Service Forwarding over SRv6 Policies
The following types of VPNs are available in enterprise network scenarios:
  L2VPN: Customer IP addresses are on the same network segment.
  L3VPN: Customer IP addresses are on different network segments.
  EVPN: Customer IP addresses are either on the same network segment (L2VPN scenario) or on different network segments (L3VPN scenario).
A tunnel policy is used by an application module to select tunnels for services. There are two types of tunnel policies:
  (Preferred mode) Tunnel type prioritizing policy: recurses services to a tunnel based on the tunnel type priority and the number of tunnels participating in load balancing.
  Tunnel binding policy: binds a destination address to a tunnel, so that the traffic of VPN services referencing the policy and destined for this address will be transmitted over the tunnel.
VPN services first select tunnels in the up state based on the tunnel policy, and then select a forwarding path from qualified tunnels.
L2VPN
L3VPN
EVPN
Color
DSCP
SRv6 Policy
SRv6 Policy Group
Tunnel policy-based tunnel type selection
A forwarding path is selected among tunnels of the same type in either of the following modes:

## Slide 120
(Short-answer question) An SRv6 SID has 128 bits. What are the three fields of an SRv6 SID?
(Short-answer question) In SIDs corresponding to SRv6 endpoint behaviors, which types of SIDs are similar to the node segments and adjacency segments in SR-MPLS?
Notes: An SRv6 SID has 128 bits and consists of the Locator, Function, and Arguments fields.
End SIDs and End.X SIDs.

## Slide 121
This course describes the concept of SRv6 network programming, SRv6 instruction sets (endpoint node behaviors, source node behaviors, and flavors), SRv6 Policy, and basic SRv6 SID configurations on Huawei NetEngine series routers.
Leveraging the programmability of 128-bit IPv6 addresses, SRv6 enriches the network functions expressed by SRv6 instructions. For example, in addition to identifying an instruction that can indicate a forwarding path, a network function can identify a VAS (e.g. firewall, application acceleration gateway, user gateway). To deploy a new network function, you only need to define a new instruction, without the need to change the protocol mechanism or deployment.
SRv6 Policy information is carried by extending new NLRIs based on MP-BGP. The controller establishes BGP IPv6 SR Policy peer relationships with forwarders to deliver SRv6 Policies to them.

## Slide 122
SRv6 Network Programming: Ushering in a New Era of IP Networks
https://datatracker.ietf.org/doc/rfc8754/
https://datatracker.ietf.org/doc/rfc8986/