## Slide 1
Datacom
General
V1.0
Lu Yueyue/WX445705
2021.08.15
Wang Xuan/00618840 & Zhu Shigeng/00261992
New

## Slide 2: IPE Key Technologies and Evolution Trends

## Slide 3
Given that IPv6 addresses are abundant, secure, and scalable, they have become an inevitable trend for network evolution. IP Enhanced Innovation (IPE) is a further development and application of IPv6 technologies and an upgrade of the IPv6-based next-generation Internet, and can create greater value for users.
This course introduces the basic concepts, development trends, and key technical applications of IPE.
This course also introduces IPv6 network evolution solutions for scenarios such as DCs, WANs, and campus networks, covering IPv6 network evolution phases and technologies and network architectures adopted in each phase.

## Slide 4
On completion of this course, you will be able to:
  Describe the technical concepts related to IPE.
  Describe the key technical applications of IPE.
  Describe IPv6 network evolution trends in scenarios such as DCs, WANs, and campus networks.

## Slide 5
Technical Background of IPE
Key Technical Applications of IPE
IPv6 Network Evolution Solutions

## Slide 6: Datacom Network: Cornerstone for Digitalization
Office
Online meeting
Manufacturing
Computing power
Enterprises
Individuals
Carrier metro/
backbone network
O&M
Security
Site
Home
Terminal
DC
The datacom network comprises a variety of datacom devices.
The digital world connects individuals, enterprises, and computing power.
The datacom network is the cornerstone for the digital world.
SD-WAN

## Slide 7: Understanding IP Forwarding on a Datacom Network Through a Network Model
R1
R2
R3
R5
PC1
PC2
Application layer
Transport layer
Network layer
Data link layer
Physical layer
Network layer
Data link layer
Physical layer
Payload
Source Port
Destination Port
Source IP: 192.168.1.1
Destination IP: 192.168.2.1
Source MAC
Destination MAC
Ethernet header
IP header
TCP header
192.168.1.1
192.168.2.1
Low bandwidth
High bandwidth
High bandwidth
Destination Network/Mask | Protocol | Next Hop
192.168.2.0/24 | OSPF | R3
… | … | …
IP is one of the most important protocols at the network layer.
A device performs IP encapsulation on the payload and forwards the payload on the network.
Network devices search their routing tables for a matching forwarding entry based on the destination IP address of the packet and forward the packet along the shortest paths.

## Slide 8: Emergence and Application of MPLS
Payload
Source Port
Destination Port
Source IP
Destination IP
Source MAC
Destination MAC
Ethernet header
IP header
TCP header
Label
EXP
BoS
TTL
Label header
MPLS header
Multiprotocol Label Switching (MPLS) is used on IP backbone networks.
MPLS combines Layer 3 routing with Layer 2 switching by applying connection-oriented label switching on connectionless IP networks. Therefore, it has flexibility of IP routing and simplicity of Layer 2 switching.
MPLS is essentially a tunneling technology and supports multiple upper-layer protocols and services.
IP packet
Label header
IP packet
Low bandwidth
Low bandwidth
Low bandwidth
IP packet
1024
IP packet
1036
IP packet
1099
IP packet
1061
MPLS headers are added to IP packets for data forwarding based on MPLS labels.
MPLS has higher forwarding efficiency, and MPLS labels can carry instruction information to guide data forwarding.
It supports applications such as traffic engineering (TE), virtual private network (VPN), and QoS.

## Slide 9: History of IP Network Transformation
Internet IP
Best effort, manual O&M
All IP
Static policy, semi-automated O&M
IPv6 + Protocol innovation + AI
5G & Cloud era
Intelligent IP
Connectivity of everything, flexible connections, intelligent O&M
IPv4
MPLS
IPE
Notes: After more than 40 years of development, IP networks have actually gone through three eras.
  The first era is the Internet era. The iconic technology of this era is best-effort forwarding represented by IPv4.
  The second era is the all-IP era. The core technology of this era is MPLS, which supports applications such as TE and E2E VPN.
  Currently, we are experiencing the intelligence era of Internet of Everything, and the core technology of this era is IPE. This era is featured by the shift from human-to-human and human-to-machine communication to the Internet of Everything. There are huge bandwidth demands, large numbers of connections, and flexible connection models. The requirements for Service Level Agreement (SLA) assurance extend from providing only connectivity to providing comprehensive capabilities (such as strict delay, jitter, and packet loss guarantee capabilities), and O&M complexity increases accordingly. As a result, a new technology is required to empower this era, and the heavy responsibility of leading networks into the IPE era falls onto the SRv6 technology family.

## Slide 10: From MPLS to SRv6
SRv6 provides a unified forwarding plane and has advantages such as simplified protocols, high scalability, and programmability.
Forwarding plane
Control plane
Classic MPLS
SR-MPLS
LDP
RSVP-TE
IGP
IGP + SR extension
Payload
Payload
Push
Swap
Pop
Payload
Payload
Push
Continue
Next
SRv6
IGP + SR extension
Payload
Payload
IPv6 + SRH
Payload
Payload
IPv6 + SRH
Payload
MPLS 222
MPLS 111
Payload
MPLS 111
Payload
MPLS 1949
MPLS 2004
Payload
MPLS 1949
MPLS 1368
Control plane simplification
Forwarding plane simplification
Simplified protocols
High scalability
Programmability

## Slide 11: IPE Technology System: Comprehensively Enabling Next-Generation Mobile Networks and the Cloud era
IPE is a technology system oriented to the next-generation mobile networks and cloud era. It uses "IPv6 + intelligent computing + protocol innovation" to meet next-generation mobile Internet bearer and cloud-network synergy requirements, such as flexible networking, fast service provisioning, on-demand services, and differentiated assurance, simplifying network O&M and improving user experience.
Any-to-any connection
SRv6
BIERv6
Experience assurance
Network slicing
In-band flow measurement
Intelligent applications
APN6
SFC
Notes: IPE technologies are innovations to the network technology system, represented by Segment Routing over IPv6 (SRv6), network slicing (FlexE), deterministic network (DetNet), in-band flow measurement (iFIT), new multicast (BIERv6), and application-aware IPv6 networking (APN6), and more.
The IPE technology system is classified into the following three categories:
  The first category provides basic connectivity and is represented by SRv6 (used to carry unicast services) and BIERv6 (used to carry multicast services). Both protocols carry and forward traffic based on the native IPv6 architecture, which eliminates the need of MPLS on the control and forwarding planes and takes advantage of IPv6's inherent scalability and other benefits.
  The second category provides experience assurance and is represented by technologies used to reserve network resources, deliver slice-based deterministic network capabilities, and provide in-band flow measurement.
  The third category comprises APN6 and SFC. APN6 provides application-level network service capabilities from the application perspective, and SFC provides flexible programming of network capabilities.
FlexE: Flexible Ethernet
DetNet: Deterministic Networking
iFIT: in-situ Flow Information Telemetry
BIERv6: Bit Index Explicit Replication IPv6 Encapsulation
APN6: Application-aware IPv6 Networking

## Slide 12: IPE Development Phases
The next-generation Internet requires more than just IPv6, which is only a starting point and platform for innovation of the next-generation Internet. The IPE roadmap facilitates systematic network evolution. With the large-scale deployment of IPv6, IPE technologies represented by SRv6 will be widely used to build intelligent, simplified, and automated next-generation networks with committed SLAs.
Phase 1: network programming
Simplified, partial autonomous networks
Based on SRv6 BE/Policy, featuring fast service provisioning, flexible path control, and automated configuration delivery.
Phase 2: user experience assurance
Experience-guaranteed, conditional autonomous networks:
Based on new technologies such as network slicing, in-band flow measurement, new multicast, deterministic forwarding, and security, featuring visualized and optimal user experience.
Phase 3: application-driven network
Application-aware, highly autonomous networks:
Application-aware network, application-driven network programming, and per-flow SLA assurance.
Cloud
Lower-level subnet
Campus network
Traditional
DC
SRv6
Slice 1
Slice 2
Default slice
Slice topology information collection
SRv6-based low delay
SRv6-based high bandwidth
Collaboration
Office
Video conferencing
Notes: Phase 1:
  SRv6 is used to simplify protocols, resolve the low efficiency problem caused by segment-based configuration and manual cross-domain configuration on traditional MPLS networks, and achieve fast E2E service provisioning across domains.
  In addition, SRv6 Policies can quickly adjust and optimize paths, improving network-wide flexibility and laying a foundation for autonomous networks.
Phase 2:
  Network slicing and FlexE are introduced to provide deterministic forwarding and differentiated dedicated network experience. Layer 2 FlexE and Layer 3 network slicing provide dedicated network resources for different services, E2E service isolation, and manageable and controllable paths. In this way, different services can be transmitted on the same network. Abundant slices ensure that each service can enjoy dedicated network experience and deterministic forwarding with controllable delay and jitter.
  Moreover, the in-band flow measurement mechanism reports service traffic status in real time, enabling network experience visualization. This allows us to determine whether service quality deteriorates in a timely manner. If service quality deteriorates, we can adjust service configurations in a timely manner to ensure optimal user experience.
Phase 3:
  In this phase, we not only need to ensure service experience, but also need to deliver experience assurance at a finer granularity (application level).
  IPv6 apps can directly carry application information in IPv6 extension headers, enabling the network to identify user and application information and provide fine-grained differentiated network channels.

## Slide 13
Technical Background of IPE
Key Technical Applications of IPE
IPv6 Network Evolution Solutions

## Slide 14: SRv6 for Flexible Forwarding Path Orchestration
A carrier provides a DDoS attack mitigation service through traffic cleaning to ensure network security.
The carrier has multiple backbone networks. Network A has only the IP routing and forwarding capability, and but has sufficient bandwidth resources. Network B has the VPN service capability, but has limited bandwidth resources.
To-Be: Native IPv6-based SRv6 VPN is deployed, allowing the service scale to expand by 10 times.
As-Is: Cleaned traffic is diverted through network A (without VPN isolation). The supported traffic scale is limited.
Internet
Cloud DC
DDoS cleaning center
Network A
Network B
1
To-be-cleaned traffic
(such as attack traffic)
Traffic will be diverted again due to a lack of the VPN service capability on the network.
2
Network B has the VPN service capability, but the supported service scale is limited during traffic diversion.
Internet
Cloud DC
DDoS cleaning center
Network A
To-be-cleaned traffic
Cleaned traffic is diverted by the native IPv6 VPN.
SRv6 only needs to be enabled on egress nodes and cloud ASBRs to implement E2E VPN.
Egress node
Cloud ASBR
SRv6
SRv6
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: This figure shows a typical SRv6 deployment case. A carrier provides network security services for customers. To prevent DDoS attacks, the traffic to the DC needs to be cleaned by the DDoS cleaning center first. Such traffic traverses the backbone network.
  The carrier has two backbone networks. Network A has high bandwidth but does not have the VPN service capability. As a result, cleaned traffic may be sent back to the cleaning center if network A is used.
  Network B has the VPN service capability but does not have high bandwidth. It is unable to support the cleaning of all service traffic.
  The volume of to-be-cleaned traffic is large. If such traffic is diverted through network A (without VPN isolation), cleaned traffic may be diverted back to the cleaning center, causing a loop. If such traffic is diverted through network B, the bandwidth resources of network B become a bottleneck as the service scale expands.
In this situation, SRv6 can be deployed on network A to direct traffic to this high-bandwidth backbone network. This implementation can provide protection for hundreds of DCs. SRv6 is easy to deploy and supports fast service provisioning.

## Slide 15: SRv6 Enables Fast E2E Service Provisioning and One-Hop Cloud Access
With the acceleration of digital transformation, cloudification has become an inevitable trend of enterprise development. Traditional private lines cannot meet the agile requirements of the cloud era in terms of provisioning speed and service quality.
To-Be: Cloud-network convergence enables one-hop cloud access and provisioning of site-to-cloud private lines within two days.
As-Is: Cloud-network separation results in slow provisioning of site-to-cloud private lines for enterprises.
Metro
Backbone
Enterprise-side deployment
Metro deployment
Backbone deployment
Cloud-side deployment
Cloud
PE
Cloud-network separation, with cloud resources interconnected case by case based on enterprise requirements.
1
Segment-by-segment deployment, multi-party collaboration required, deployment taking 1 to 2 months.
2
CPE
Metro
Cloud backbone
Cloud
Cloud PE
Cloud-network convergence, with cloud PEs pre-integrated with numerous cloud resources.
1
E2E EVPN over SRv6 deployed between CPEs and cloud PEs to enable one-hop cloud access.
2
EVPN over SRv6
CPE
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: Currently, large numbers of enterprises are deploying their services on the cloud. Carriers must consider how to quickly provision site-to-cloud private lines for enterprises.
  Traditional private lines, such as MPLS private lines, may involve multiple ASs. Different ASs are managed and maintained by different management teams. The provisioning of a private line for one-hop cloud access involves collaboration and coordination among multiple departments.
  With SRv6, the deployment is easy. An E2E SRv6 logical private line can be established between the enterprise CPE and cloud PE to carry cloud-based services, achieving one-hop cloud access. Moreover, private line provisioning is very fast in this case.
As shown in the figure, carriers want to build a cloud backbone network to enhance their market competitiveness in the cloud era by delivering one-hop cloud access and cloud-network convergence capabilities to enterprises.

## Slide 16: SRv6 Implements Delay-based Path Computation and Flexible Optimization
The backbone network of a carrier is a native IP network, which provides best-effort IP forwarding for services. The carrier wants to provide differentiated services for customers and increase revenue by improving the user experience of delay-sensitive services.
To-Be: SRv6-based low-delay and differentiated service experience
As-Is: unified service bearer, best-effort IP forwarding
DC
Metro 1
Metro 2
Backbone
Unified service bearer, no service differentiation
The network loads are uneven. Service paths are adjusted based on cost, complicating deployment.
2
Services treated equally regardless of service types.
1
There is no VPN service capability, and services are not isolated.
3
DC
Metro 2
Backbone
Common links
Low-delay links
Network information collection
Low-delay path orchestration
The controller orchestrates service paths based on service delay requirements.
1
Some services are flexibly and dynamically steered to other paths based on link loads and delay.
2
SRv6 L3VPN provides service isolation.
3
Metro 1
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: As shown in the figure, the backbone network of a carrier is a native IP network, which provides best-effort IP forwarding for services. The carrier's DC provides cloud services for users, and some of these services are delay-sensitive. The current network does not differentiate delay-sensitive services from common services during service transmission, resulting in poor user experience of delay-sensitive services. Moreover, because services are forwarded along least-cost paths, network loads are uneven, and network management and maintenance are complex. Against this backdrop, the carrier wants to provide differentiated services for customers and increase revenue by improving the user experience of delay-sensitive services.
The iMaster NCE + SRv6 solution measures the delay of each link on the network and computes paths based on the shortest delay. This solution allows public cloud-based services to travel along the shortest-delay paths, improving the competitiveness of the public cloud.

## Slide 17: Multi-Service Bearer Through Network Slicing in a Power Company
Relay protection
Production O&M
Video surveillance
Dispatch phone
WAMS
Office phone
Campus surveillance
DC
Office automation
Customer service
Slice 1
Slice 2
Slice 3
Slice 4
Flexible, convenient service deployment.
Support for network evolution over the next 10 years:
Smooth upgrade to 100G/200G
Smooth evolution to SRv6 + EVPN
Unified bearer: The controller deploys network resources in a unified manner to carry power services, implementing intelligent optimization.
Physical network slicing: The TDM-based FlexE technology divides the physical network into multiple slices on demand to isolate different services and ensure service SLAs.
Office services
Production services
Various office services
Dispatch phone
Video surveillance
Production O&M
Relay protection
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: WAMS: Wide Area Measurement System

## Slide 18: Application of iFIT to One-Financial-WAN-for-All-Services Scenarios
In a one-financial-WAN-for-all-services scenario, SRv6 can quickly and conveniently establish basic network connections between clouds and various access points, ensuring efficient service provisioning.
Solution highlights:
In SRv6 scenarios, tunnel-level iFIT can be enabled to measure the quality of each SRv6 segment list and select the optimal link. The link currently in use is periodically compared with the optimal link for path selection and optimization, implementing intelligent traffic steering.
One controller is deployed to perform centralized O&M on the entire financial network and implement E2E management and scheduling.
Cloud
CPE
Outlet
Telemetry
iFIT measurement domain
Branch
Head office
Aggregation layer
Core layer
Cloud
Cloud
Candidate path 1
Candidate path 2
...
SRv6
NETCONF
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: One WAN for all services is a technology that provides cross-domain network services through coordination among different networks. In the financial industry, tier-2 banks, outlets, subsidiaries, and external organizations access the head office DC through tier-1 banks, which aggregate service traffic and forward aggregated traffic to the bank core network.
The financial industry has high requirements on SLA performance. With the development of banking services, diversified service types have emerged in outlets. In addition to traditional production and office services, there are also security protection, IoT, public cloud, and other services. This poses higher O&M requirements on the one-financial-WAN-for-all-services scenario. Against this backdrop, Huawei proposes the iFIT tunnel-level measurement solution.

## Slide 19: Application Trends of Multicast Technologies
Currently, video traffic accounts for a large proportion of Internet traffic, including video calls, video sharing, and video conferences. High Definition (HD) visual and new interactive videos may become the main social means in the future, and media gradually evolve to Virtual Reality (VR)/Augmented Reality (AR). These new services pose new requirements on network bandwidth and user experience.
Multicast Technical Benefits
Reduced server load
Reduced network load
New services
VR
Video streaming
Online education
HD video
Video conferencing
While the potential applications of multicast are booming, the trend of adopting IPv6-based networks becomes more and more prominent. As IPv6 becomes more widely adopted and new service scenarios require higher bandwidth and better user experience, multicast technologies on IPv6 networks need to continuously evolve in order to keep pace with new service scenarios and technology development trends.
SRv6
Network Slicing
In-band Flow Measurement
New Multicast

## Slide 20: New Multicast Technology
Compared with conventional multicast protocols, Bit Index Explicit Replication (BIER)/Bit Index Explicit Replication IPv6 Encapsulation (BIERv6) uses the basic IGP and unicast routing forwarding mechanisms combined with the BitString mechanism to implement multicast packet replication and forwarding.
R1
R4
R5
R6
R7
R2
R3
My BFR-ID is 2.
I want to watch multicast channel X.
1
1
1
Multicast client
Multicast client
Multicast client
My BFR-ID is 3.
I want to watch multicast channel X.
My BFR-ID is 5.
I want to watch multicast channel X.
2
Combines 2, 3, and 5 into a BitString and encapsulates the BitString into packets so that the packets can reach R4, R5, and R7.
The transit node replicates packets according to the BitString generated based on BFR-IDs.
3
3
Basic Concepts of Bit Index Explicit Replication (BIER)
BIER domain: network domain that supports BIER forwarding. A BIER domain can be divided into multiple sub-domains, and each BIER domain contains at least one sub-domain.
Bit Forwarding Router (BFR): a router that supports BIER forwarding.
Bit Forwarding Ingress Router (BFIR): ingress router in a BIER domain.
Bit Forwarding Egress Router (BFER): egress router in a BIER domain.
Edge BFR: BFIRs and BFERs are collectively referred to as edge BFRs. That is, edge BFRs refer to source and destination nodes in a BIER domain.
BFIR Forwarding Router Identifier (BFR-ID): dedicated identifier of an edge BFR, with the value ranging from 1 to 65535.
BitString: 256-bit (or 32-byte) set consisting of BFR-IDs of destination nodes. The position or index of each bit in the BitString indicates a specific edge node.
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: BIER overview:
  This multicast technology encapsulates a set of destination nodes of multicast packets in a BitString in the packet header before sending the packets. With this multicast technology, transit nodes do not need to establish a multicast distribution tree (MDT) for each multicast flow, or maintain the states of multicast flows. Instead, the transit nodes replicate and forward packets according to the BitString in the packet header.
  In BIER, each destination node is a network edge node. For example, on a network with no more than 256 edge nodes, each node needs to be configured with a unique value ranging from 1 to 256. In this case, the set of destinations is represented by a 256-bit (32-byte) BitString, and the position or index of each bit in the BitString indicates an edge node. This explains the meaning of Bit Index Explicit Replication.
Advantages of BIER:
  Supports large-scale multicast service scenarios and reduces resource consumption as BIER does not need to establish an MDT for each multicast flow or maintain the states of multicast flows.
  Improves multicast group joining efficiency of multicast users in SDN network scenarios because requests of the multicast users do not need to be forwarded along the MDT hop by hop, and instead their requests are directly sent by leaf nodes to the ingress node. This is more suitable for the controller on an SDN network to directly deliver the set of destinations to which multicast packets are to be sent after collecting the set.
BIERv6 inherits the advantages of BIER and uses IPv6 to program paths, functions, and objects, facilitating multicast forwarding on SRv6-based networks.

## Slide 21: BIER Multicast Traffic Forwarding Mechanism
To send multicast traffic of (S1, G1) to PE1, PE2, and PE3, PE4 encapsulates a multicast packet with the BitString (0111). The multicast traffic is sent as follows:
  PE4 -> P2: In the packet sent from PE4 to P2, the BitString is 0111 (set of the BFR-IDs of PE1, PE2, and PE3).
  P2 -> PE3: In the packet sent from P2 to PE3, the BitString is 0100 (containing only the BFR-ID of PE3).
  P2 -> P1: In the packet sent from P2 to P1, the BitString is 0011, which contains the set of BFR-IDs of PE1 and PE2, with the BFR-ID of PE3 removed.
  P1 -> PE1: In the packet sent from P1 to PE1, the BitString is 0001 (containing only the BFR-ID of PE1).
  P1 -> PE2: In the packet sent from P1 to PE2, the BitString is 0010 (containing only the BFR-ID of PE2).
PE4, edge node, BFR-ID: 4
P2
Transit node
P1
Transit node
PE3, edge node, BFR-ID: 3
PE1, edge node, BFR-ID: 1
PE2, edge node, BFR-ID: 2
0:1000
Data packet
0:0100
Data packet
0:0001
Data packet
0:0010
Data packet
ID | F-BM | NBR
1 | 0111 | P2
2 | 0111 | P2
3 | 0111 | P2
4 | 1000 | PE4
BFR-PE4 BIFT
ID | F-BM | NBR
1 | 0011 | P1
2 | 0011 | P1
3 | 0100 | PE3
4 | 1000 | PE4
BFR-P2 BIFT
ID | F-BM | NBR
1 | 0001 | PE1
2 | 0010 | PE2
3 | 1100 | P2
4 | 1100 | P2
BFR-P1 BIFT
The ID refers to a BFR-ID. To forward packets to the node of a specified BFR-ID, the device needs to query the entry corresponding to the BFR-ID.
F-BM is short for Forwarding BitMask. It indicates the set of BIER domain edge nodes that are reachable through the next hop after packets are replicated and sent to the next hop.
NBR is short for neighbor. It indicates the next hop neighbor through which packets can reach a node of a specified BFR-ID.
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: Bit allocation fundamentals: BIER floods the mapping between bit positions (BFR-IDs) of nodes and prefixes through IS-IS LSPs (IS-IS for BIER is used as an example). Devices learn the complete BIFT (BIER neighbor table) through flooding. The BIFT has the following characteristics:
  In the neighbor table, each directly connected neighbor has one entry.
  Each entry contains information about the edge nodes that are reachable to a neighbor.
BIFT: Bit Index Forwarding Table

## Slide 22: BIERv6
In terms of unicast forwarding, SRv6, which is based on the IPv6 data plane, has developed rapidly and surpassed SR-MPLS, which is based on the MPLS data plane. In terms of multicast, however, a solution was urgently needed to use the BIER architecture and encapsulation in order to implement MPLS-independent technologies and match the development trend of IPv6 networks. Against this background, BIERv6 was proposed in the industry.
BIERv6 inherits the core design concept of BIER. It uses the BitString to guide multicast packet replication and forwarding to specified receivers, eliminates the need for transit nodes to establish MDTs, thereby implementing stateless forwarding.
Ethernet
MPLS Label
BIER
VPN Label
Payload
Ethernet
IPv6 Header
(VPN)
BIER
Payload
BIER encapsulation
BIERv6 encapsulation
The main difference between BIERv6 and BIER is that BIERv6 is a multicast solution based on native IPv6 rather than MPLS labels.
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: Advantages of BIERv6:
  Simplified network protocols:
    BIERv6 uses IPv6 addresses to carry Multicast VPN (MVPN) and GTM services, further simplifying protocols and eliminating the need to allocate, manage, and maintain MPLS labels.
    BIERv6 has high extensibility as it complies with the design concept of SDN and network programming.
  Simplified deployment and O&M:
    BIERv6 uses an IPv6 extension header to carry BIER forwarding instructions, eliminating the need for MPLS label-based forwarding. IPv6 extensibility facilitates the evolution and addition of new features.
    Because BIERv6 is deployed only on the ingress and egresses, transit nodes are unaware of multicast service changes. When the network topology changes, there is no need to withdraw or re-establish numerous MDTs, thereby greatly simplifying O&M.

## Slide 23
Notes:   High network reliability:
    BIERv6 uses IGP extension to flood BIER information, using which each node establishes a multicast forwarding table for data forwarding. In addition, BIERv6 uses unicast routes to forward traffic, meaning that there is no need to establish MDTs. This eliminates the need for complex protocol processing, such as multicast source sharing and SPT switching.
    In addition, BIERv6 reduces the number of entries that need to be stored because it does not need to maintain per-flow MDT states. If a fault occurs on the network, devices only need to update entries in their BIFTs after the underlay route convergence. This ensures fast BIERv6 convergence if a fault occurs, thereby improving reliability and enhancing user experience.

## Slide 24: BIERv6 Application in an IPTV Scenario
IP video services include live TV (such as news, sports events, movies and TV series, and live webcasting), video on demand (VOD), and video surveillance. Video transmission service applications such as 4K IPTV, 8K VR, smart city, smart home, autonomous driving, telemedicine, and safe city are expected to grow dramatically in the near future, especially in countries and regions with fast economic development.
In the figure, MVPN over BIERv6 is deployed on the public network to carry IPTV traffic. BIERv6 multicast technology greatly reduces the network load and improves user experience (for example, it ensures fast VOD, clear images, and smooth playback).
In addition, this solution features simple deployment, O&M, and capacity expansion and is suitable for large-scale deployment.
4K
4K
Source
Sender PE
Sender PE
ACC
ACC
OLT
OLT
4K TV
4K TV
IP backbone network
IP metro network
Multicast traffic
SRv6
Network Slicing
In-band Flow Measurement
New Multicast
Notes: IPTV: Internet Protocol Television
OLT: Optical Line Termination

## Slide 25
Technical Background of IPE
Key Technical Applications of IPE
IPv6 Network Evolution Solutions

## Slide 26: General Principles for IPv6 Network Evolution
The purpose of enterprise network evolution to IPv6 is to build IPv6 capabilities on the existing network architecture and meet the requirements of current network service development. From the perspective of enterprise services, IPv6 reconstruction requires that the original IPv4 services be sustainable during network evolution and upgrade and the network security level after evolution be higher than or equal to that of the original IPv4 network.
Considering reconstruction cost, technology evolution, and impact scope, it is recommended that enterprise IPv6 reconstruction comply with the following principles:
  Smooth evolution: IPv6 network upgrade and reconstruction involve the changes of basic protocols. During network evolution, ensure that existing users are unaware of these changes and existing services are migrated smoothly.
  Future readiness: Seize IPv6 evolution and upgrade opportunities and build an advanced next-generation enterprise IPv6 network architecture to fully support the long-term development and stable operation of enterprise service systems to avoid repeated network construction and investments.
  Economical feasibility: A proper IPv6 upgrade and evolution solution should be selected from the overall perspective based on the current enterprise network system conditions to properly reuse existing devices and avoid asset wastes.
  Architecture optimization: The IPv6 evolution of enterprise networks provides opportunities to update or reconstruct the enterprise system management architecture, such as adding strict control of enterprise addresses and unified management of DNS resources.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Enterprise services can be classified into Internet services, DMZ services, and enterprise-built service systems. Internet services and DMZ services depend on external network applications and user environments and require long-term coexistence of IPv4 and IPv6 user access. This factor must be considered during IPv6 reconstruction of enterprise networks.

## Slide 27: Logical Architecture Panorama of Enterprise Networks
Production system
Egress
Access
Access
Production campus
Egress
Access
Access
Large- and medium-sized office campuses
Egress
Access
Access
Small branch campus
WAN
Enterprise-built WAN
Carrier private line
Internet private line
Access over a dedicated network
Access over a dedicated network
…
…
DC 1
DC N
Internet
Overview
DC
WAN
Other Systems
Campus Network
Notes: DCN:
  Based on the service scope, enterprise DC services can be classified into external services and internal applications.
    The front-end servers for external services are generally deployed in the DMZ of the DC and connect to external user devices through the Internet egress zone.
    Internal applications mainly involve the DC's internal service networks (such as networks in the WAN egress zone and service zone).
  From the perspective of service reconstruction, the DCN can be classified into the internal application network, DMZ (for external services), Internet egress, and internal service network during IPv6 evolution and upgrade planning.
WAN:
  Multiple backhaul solutions are available for interconnection between enterprise branches, such as enterprise-built WAN, carrier MPLS L2VPN/L3VPN, and Internet private line.
  The IPv6 evolution of enterprise WANs mainly considers the WAN upgrade policy.

## Slide 28
Notes: Campus network:
  Office campuses can be classified into HQ campuses and branch campuses. The two types of campuses have different networking scales. Moreover, branch campuses may have multiple WAN backhaul access modes, such as enterprise-built WAN and carrier private line. Therefore, targeted design is required during IPv6 evolution and upgrade design.
  A large number of production terminals and systems are deployed in production campuses. Most production service flows are closed within campuses. The production systems and terminals on production campuses have long lifecycles. Therefore, networks must support IPv4/IPv6 dual-stack services within a long period of time, and IPv4 + IPv6 interworking must be considered.

## Slide 29: IPv6 Network Migration Process
The entire IPv6 migration process for enterprise networks can be divided into three phases:
  Phase 1: Prioritize pipe upgrade and Internet egress upgrade, including DMZ upgrade, WAN upgrade, and IPv6 test field construction.
  Phase 2: Fully upgrade internal networks, such as upgrading the DCN and production campus networks and reconstructing office campus networks. Moreover, configure services to preferentially access IPv6 networks.
  Phase 3: Switch internal applications to IPv6 channels and retain the IPv4 capability for external Internet access.
v4
v4
v4
v4
v4
v4
v4
v4
v4
v4
v4/v6
v4/v6
v4/v6
v4/v6
v4
v4
v4
v4
v4/v6
v4
v4/v6
v4
v4/v6
v4/v6
v4/v6
v4/v6
v4/v6
v4/v6
v4/v6
v4
v6
v6
v4/v6
v4/v6
v6
v4/v6
v4/v6
v4/v6
v4/v6
v4
v6
v6
v6
v6
v6
v6
v6
v6
v6
v6
Now
Phase 1
Phase 2
Phase 3
Future
DMZ
public service
Production campus
network
Internal applications
Internet egress
DCN
WAN
HQ campus
Branch campus
Production system
DC
WAN
Office
Production campus
Overview
DC
WAN
Other Systems
Campus Network
Notes: The overall IPv4-to-IPv6 network migration principle is "DCN first, WAN second, and campus network reconstruction on-demand".
  Phase 1: Deploy dual-stack services in the DC's public service and test zones and IPv4 single-stack services on the WAN's underlay network and dual-stack services on the WAN's overlay network, and pilot dual-stack services on the campus network .
  Phase 2: Gradually apply dual-stack to the DC's internal applications and the campus network's office campus part and apply dual-stack to the campus network's production campus part.
  Phase 3: Comprehensively apply IPv6 single stack to the DC's internal applications and ensure that the WAN gradually evolves to IPv6-only networks.

## Slide 30: IPv6 Network Evolution Solutions
Network Layer | Phase 1: Dual-Stack Service | Phase 2: Dual-Stack Service | Phase 3: Single-Stack Service
Management and control layer | IPv4 management channel | IPv4/IPv6 dual-stack management channel | IPv6 management channel
DCN | Traditional DC: dual stack | VXLAN underlay IPv6 + overlay dual stack | VXLAN underlay IPv6 + overlay IPv6
 | VXLAN underlay IPv4 + overlay dual stack |  | 
Bearer WAN | Dual stack over MPLS (6VPE) | Dual stack over SRv6 | IPv6 over SRv6
 | Native IP dual stack |  | 
 | Dual stack over SRv6 |  | 
Campus network | Traditional campus network: dual-stack |  | Virtualized campus network: VXLAN underlay IPv6 + overlay dual stack
 | Virtualized campus network: VXLAN underlay IPv4 + overlay dual stack |  | 
Overview
DC
WAN
Other Systems
Campus Network
Notes: DCN:
  The reconstruction solutions for the Internet access zone include NAT64, IVI, and dual-stack reconstruction. It is recommended to use the dual-stack solution to provide IPv6 addresses and service capabilities.
    NAT64 is limited by session table specifications and consumes a lot of resources. With the increase of IPv6 terminals, NAT64 will become a performance bottleneck for IPv6 service development. Therefore, NAT64 is applicable only to the early deployment of IPv6 services and is not recommended to be a target solution.
    The IPv6 address structure of the IVI is limited and does not meet the IPv6 address planning principles. Therefore, the IVI is not recommended for large-scale deployment.
  Internal network resource pool reconstruction mainly uses dual-stack solutions, including VXLAN underlay IPv4 + overlay dual stack and VXLAN underlay IPv6 + overlay dual stack.
    VXLAN underlay IPv4 + overlay dual stack can be used for initial dual-stack reconstruction to quickly provide IPv6 service bearer capabilities.
    VXLAN underlay IPv6 + overlay dual stack can be used for new DCN deployment and existing DCN reconstruction. This facilitates gradual evolution to IPv6-only networks.

## Slide 31
Notes: WAN:
  WAN IPv6 reconstruction solutions mainly include dual stack, 6VPE, and IPE.
    Networks without VPN services can use native IPv4 and native IPv6 dual-stack forwarding. Increasing SLA requirements, such as requirements for on-demand optimization and intelligent O&M, will gradually drive network evolution to IPE, so that these networks can provide better service assurance and experience capabilities. Finally, these networks will evolve to IPv6-only networks.
    For networks with VPN services, it is recommended that they directly evolve to IPE to provide IPE bearer for interconnection between campuses and DCs.
Campus network:
  Campus IPv6 reconstruction solutions mainly include dual stack, VXLAN underlay IPv4 + overlay dual stack, and VXLAN underlay IPv6 + overlay dual stack.
    For campus dedicated networks that do not require VPN services, it is recommended to use dual stack to provide IPv6 services, gradually evolve these networks to IPE to provide high-order features such as SDN, fast service cloudification, on-demand optimization, and intelligent O&M, and finally evolve these networks to IPv6-only networks.
    For networks that require VPN isolation, it is recommended to use VXLAN underlay IPv4 + overlay dual stack to quickly provision IPv6 services and implement SDN, gradually evolve these networks to IPE, and finally evolve these networks to IPv6-only networks.

## Slide 32: DCN IPv6 Evolution Overview
Evolution Strategies
Internet zone (new deployment is recommended):
Internet access zone: dual stack
Internet resource pool: new fabric deployment, VXLAN underlay IPv6 + overlay dual stack
Intranet resource pool:
Live network reconstruction: VXLAN underlay IPv4 + overlay dual stack
New fabric deployment: VXLAN underlay IPv6 + overlay dual stack
OAM zone:
Live network reconstruction: dual stack
Other zones (WAN access area & core area):
Live network reconstruction or new deployment: dual stack
OAM zone
Management service zone
Out-of-band management zone
Internet resource pool (DMZ)
Intranet resource pool
Leaf
FW
WAN
Intranet core
Extranet core
Anti-DDoS
Router
AS
IPS
Internet access zone
DS
AS
DS
AS
FW
FW
Spine
Spine
VXLAN domain
VXLAN domain
Leaf
FW
Border-Leaf
DC-CE
DC-PE
Border-Leaf
WAN access zone
Internet
FW
Overview
DC
WAN
Other Systems
Campus Network
Notes: DCN architecture:
  The underlay network refers to the physical network or infrastructure network. It is required that any two nodes on the physical network be routable to each other. The spine-leaf architecture is recommended for underlay networking.
    A spine node is a core node on a VXLAN fabric network, which provides high-speed IP forwarding and connects to leaf nodes using high-speed interfaces.
    A leaf node is an access node on a VXLAN fabric network, which connects various network devices to the VXLAN network. Different access objects are classified into border leaf nodes, server leaf nodes, and service leaf nodes.
  The overlay network is a virtualized network built on the underlay network to carry applications over the physical network while remaining isolated from other service networks.

## Slide 33
Notes: VXLAN is deployed to construct fabric resource pools for intranet and Internet resource pools on a DCN.
DC services mainly involve external public services and enterprise internal applications. Generally, the external public service system is deployed in the DMZ of a DC. To provide services for IPv6 users, perform IPv6 upgrade for external public services in the DMZ. The upgrade involves the interconnection egress where the DMZ is located, the DMZ network, and the corresponding public service system. The dual-stack solution is recommended for the overall evolution policy, so that IPv4 and IPv6 Internet users can both access public services.
AS: access switch
DS: distributed switch, which corresponds to the aggregation switch on the traditional network.
IPS: intrusion prevention system
Anti-DDoS: anti-distributed denial of service

## Slide 34: IPv6 Reconstruction for the DC's Internet Access Zone
IPv4 Internet resource pool (DMZ)
Extranet core
Anti-DDoS
Router
AS
IPS
IPv4
Internet access zone
Firewall
Spine
VXLAN domain
Leaf
Firewall
Border-Leaf
IPv4 Internet
Anti-DDoS
Router
AS
IPS
Newly deployed IPv6 Internet access zone
Firewall
IPv6 Internet
IPv6 Internet resource pool (DMZ)
Spine
VXLAN domain
Leaf
Firewall
Border-Leaf
Carrier address
Static route
Public network address
BGP route
Newly deployed IPv6 Internet access zone
A general way to reconstruct the Internet access zone is to deploy a new IPv6 Internet access zone.
Solution 1: Deploy NAT64 at the egress of the Internet access zone.
Solution 2: Perform dual-stack reconstruction in the Internet access zone.
Solution 3: Deploy a new IPv6 Internet access zone.
Deploy new egress lines:
New IPv6 lines are usually used to prevent production accidents.
The IPv6 Internet access zone can interconnect with the carrier network through static routes or EBGP4+ and support IPv6 user access.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Internet zone evolution strategies:
  Solution 1: Deploy NAT64 at the egress of the Internet access zone. If existing DC services remain in IPv4 single-stack mode but IPv6 services need to be quickly provided due to other factors, NAT64 can be deployed for IPv4 servers in the DC's DMZ to temporarily provide IPv4/IPv6 dual-stack services through the NAT64 gateway.
  Solution 2: Perform dual-stack reconstruction in the Internet access zone and DMZ. If the Internet zone (including the DMZ) supports IPv6 well and devices are far from reaching the end of their lifecycle, it is recommended that these devices be reused. You can deploy the dual-stack solution in the existing Internet access zone and DMZ to complete the reconstruction at a low cost.
  Solution 3: Deploy a new Internet access zone and DMZ. Reusing existing devices during IPv6 network reconstruction may involve software and hardware upgrades or partial hardware replacement, which affects IPv4 services. To ensure enterprise DMZ service continuity and zero impact on live network IPv4 services, deploy an IPv6-only Internet access zone and DMZ. IPv4 users access the IPv4 DMZ through the IPv4 Internet access zone, and IPv6 users access the IPv6 DMZ through the IPv6 Internet access zone.
Egress route selection:
  Single-egress Internet access: Static routes are preferred.
  Multi-egress Internet access: BGP routes are preferred. To ensure load balancing and reliability, BGP route attributes can be used to control route selection.

## Slide 35: IPv6 Reconstruction for DC Intranet Resource Pools
Application scenario: Devices on the live network are approaching the end of their lifecycles or do not support underlay or overlay IPv6 deployment.
Overall policy: Create an intranet resource pool that supports VXLAN underlay IPv6 + overlay dual stack.
Step 1: Traditional IPv4 network
Step 2: IPv6 SDN network
Step 3: IPv6 SDN network
Intranet core
Intranet resource pool
Leaf
Firewall
Spine
Border-Leaf
Intranet core
Intranet resource pool
Leaf
Firewall
Spine
Border-Leaf
Core (IPv4)
Underlay IPv4
Core (dual stack)
Underlay IPv6
Overlay dual stack
(MP-BGP EVPN)
Overlay IPv4
Intranet core
Intranet resource pool
Leaf
Firewall
Spine
Border-Leaf
Core (IPv6)
Underlay IPv6
Overlay IPv6
(MP-BGP EVPN)
Make preparation for IPv6 resource pool network evolution, such as IPv6 address planning, device reuse evaluation, solution design, and service impact evaluation.
Deploy a network based on the fabric granularity. Use IPv6 for the underlay layer, and IPv4/IPv6 dual stack for the overlay layer. Establish dual-stack connections between border leaf nodes and core nodes and between border leaf nodes and firewalls.
Finally, after application reconstruction, disable IPv4 at the overlay layer, so that the DC's internal network resource pool uses IPv6 single stack.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Resource pool/server deployment:
  A general way to prevent production accidents and service interruption caused by the upgrade of original IPv4 services is to deploy new IPv6 resource pools/servers.
  If the DC is a traditional DC, it is recommended that new technologies, such as SDN, be deployed in the new resource pools.

## Slide 36: WAN IPv6 Evolution Overview
The WAN is mainly used to carry services. Currently, the industry has reached a consensus that IPv4 and IPv6 will coexist for a long time.
  For an existing WAN where MPLS is deployed, using 6VPE for reconstruction is recommended. Only edge nodes need to be upgraded or have their hardware replaced. P nodes do not need to be reconstructed. Deploying IPv6 is like introducing new services and has little impact on original maintenance. Therefore, this solution is suitable for evolution from existing networks to IPv6.
  SRv6 can be considered during new WAN planning and design. SRv6 is the preferred technology for SDN-based networks in the IPv6 era. SRv6 features high scalability, good application compatibility, and strong programming capabilities. SRv6 can meet the requirements of future service changes and is suitable for evolving new networks to IPv6.
Dual stack
6VPE
IPE
IPv6-only networks are deployed once and for all, with all network traffic carried using IPv6.
IPE supports service isolation.
IPv4/IPv6 dual stack must be enabled on all Layer 3 devices.
Layer 3 devices must be reachable to each other through dual-stack routes.
The network needs to maintain two protocol stacks, increasing complexity.
IPv4/IPv6 dual stack must be enabled on edge nodes. The edge nodes must be enabled to exchange VPNv6 routing information with their original MP-IBGP peers.
The intermediate nodes only require IPv4 single stack (MPLS) deployment and do not need to be reconstructed.
Overview
DC
WAN
Other Systems
Campus Network

## Slide 37: IPv6 Evolution Strategy for the Bearer WAN (New Deployment Scenario)
Application scenario: Devices on the live network are approaching the end of their lifecycles or devices on the live network do not support IPE.
Cloud
Lower-level subnet
Campus network
Traditional
DC
IP/MPLS
IPE
Cloud
Traditional DC
Cloud
Traditional DC
IPE
Step 1: Prepare for the evolution.
Step 2: Construct the network and cut over services.
Step 3: Remove the legacy network after service cutover.
IP/MPLS
Create an IPE single-stack network to carry IPv6 services.
Deploy IPE single stack on the entire WAN to carry IPv6 services.
Lower-level subnet
Campus network
Lower-level subnet
Campus network
Overview
DC
WAN
Other Systems
Campus Network
Notes: Overall strategy: Deploy IPE single stack to carry both IPv4 and IPv6 services, and gradually evolve office, production, management, and other services from IPv4 to IPv6.
Step 1: Prepare for the evolution.
  Address application: Apply for IPv6 addresses based on enterprise requirements from address management organizations or carriers.
  Live network evaluation: Evaluate live network conditions, covering the network infrastructure, security infrastructure, service support systems, and service applications.
  Integration verification: Design and verify the IPE evolution solution and prepare a feasibility report.
  Network planning: Formulate the IPE network construction specifications and evolution solution to support smooth evolution to IPv6-only networks.
Step 2: Construct the network and cut over services.
  Network construction: Build an IPE network based on the network plan and deploy capabilities such as SRv6, network slicing, in-band flow measurement, and SDN.
  Security construction: Security devices must support IPv6 security protection. Network devices interwork with security devices to ensure that IPv6 has the same or even stronger security protection capabilities compared with IPv4.

## Slide 38
Notes:   Acceptance test: Perform service tests based on the new IPv6 network to determine whether the network meets service SLA, network security, and OAM requirements.
  Service cutover: Gradually migrate services from the traditional WAN to the new IPv6 WAN based on diversified service requirements.
Step 3: Remove the legacy network after service cutover.
  O&M observation: After services are migrated from the traditional network to the IPE network, set an observation period to observe the service running status.
  Legacy network removal: Remove the legacy network only when there are no major service issues during the observation period. The IPE evolution of the WAN is then complete.

## Slide 39: IPv6 Evolution Strategy for the Bearer WAN (Upgrade Scenario)
Application scenario: Devices on the live network have not reached the end of their lifecycles and can be upgraded to support IPE.
Step 1: Prepare for the evolution.
Step 2: Reconstruct the edge and enable basic IPE capabilities.
Step 3: Reconstruct the entire network and enable higher-order IPE capabilities.
Cloud
Lower-level subnet
Campus network
Traditional
DC
Cloud
Lower-level subnet
Campus network
Traditional
DC
IPE
Cloud
Lower-level subnet
Campus network
Traditional
DC
Coexistence of IP/MPLS and IPE
IP/MPLS
Upgrade some devices to support IPE and deploy SRv6 and IP/MPLS, so that these devices can transmit both IPv6 and IPv4 services.
Upgrade all WAN devices to support IPE and deploy SRv6 for these devices to transmit IPv6 services.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Overall strategy: Upgrade and replace nodes one by one from the edge to the core. Gradually deploy IPE features (simple features first, then complex features) and cut over services (common services first, then critical services).
Step 1: Prepare for the evolution.
  Address application: Apply for IPv6 addresses based on enterprise requirements from address management organizations or carriers.
  Live network evaluation: Evaluate live network conditions, covering the network infrastructure, security infrastructure, service support systems, and service applications.
  Integration verification: Design and verify the IPE evolution solution and prepare a feasibility report.
  Network planning: Formulate the IPE network construction specifications and evolution solution to support smooth evolution to IPv6-only networks.
Step 2: Reconstruct the edge and enable basic IPE capabilities.
  Edge device upgrade: Upgrade edge devices (cloud, Internet egress, and campus egress PEs preferred) to support IPE.
  IPE basic capability deployment: Deploy both SRv6 and traditional IP/MPLS on upgraded devices. Configure new and old devices to interwork through IP/MPLS, and use SRv6 between new devices. Deploy a controller for network-wide management and control.

## Slide 40
Notes:   IPv6 security deployment: For services that have been upgraded to IPv6, upgrade related security devices to support IPv6 security protection.
  Common service cutover: Use SRv6 to carry some common services and verify the basic capabilities of the IPE solution.
Step 3: Remove the legacy network after service cutover.
  Core device upgrade: Upgrade core devices to ensure that IPE is supported on the entire network.
  High-order IPE capability deployment: Deploy high-order capabilities such as SRv6, network slicing, in-band flow measurement, SDN, and network-security association.
  Service cutover: Gradually migrate services from IP/MPLS to IPE based on diversified service requirements.
  Redundant configuration deletion: After service migration, set an observation period and observe the service running status. If services run properly during the observation period, delete IP/MPLS configurations to complete the IPE evolution of the WAN.

## Slide 41: SRv6 Solution Overview
SRv6 can be considered during new WAN planning and design. SRv6 is the preferred technology for SDN-based networks in the IPv6 era. SRv6 features high scalability, good application compatibility, and strong programming capabilities, which can fully meet the requirements of future service changes on networks. Therefore, SRv6 has become the best network bearer technology available and is suitable for evolving new networks to IPv6.
Overall SRv6 bearer solution
For different service scenarios, the SRv6 WAN bearer solution uses SRv6 at the overlay layer to carry Layer 2, IPv4, and IPv6 services and IPv6 single stack at the underlay layer. This design prevents the IGP from maintaining both IPv4 and IPv6 protocol stacks, reducing the pressure on device protocol maintenance.
The underlay layer uses routing protocols such as IS-IS for IPv6 and MP-BGP to advertise basic routes (such as loopback routes and SRv6 locator routes), delivering basic IPv6 route reachability and laying a foundation for SRv6 to carry overlay services.
The overlay layer selects different BGP address families based on service types to transmit user information (such as IP and MAC address information).
PE1
ASBR1
PE2
ASBR2
PE3
ASBR3
PE4
ASBR4
IGP
MP-BGP
IGP
EVPN VPWS over SRv6
L3VPNv4/EVPN L3VPNv4 over SRv6
L3VPNv6/EVPN L3VPNv6 over SRv6
Underlay
Overlay
Basic routing
Layer 2 service
IPv4 service
IPv6 service
MP-BGP
MP-BGP
Overview
DC
WAN
Other Systems
Campus Network
Notes: Overlay service deployment suggestions:
  Layer 2 services: Use SRv6 EVPN as the bearer protocol to provide P2P and P2MP connection models. Compared with traditional Virtual Switching Instances (VSIs) and Pseudo Wires (PWs), EVPN features simple deployment, high bandwidth utilization, and fast convergence. EVPN is the best choice for L2VPN service bearer.
  Layer 3 IPv4 services: Use either SRv6 L3VPN or SRv6 EVPN L3VPN. Using SRv6 EVPN L3VPN is recommended.
  Layer 3 IPv6 services: Use either SRv6 L3VPNv6 or SRv6 EVPN L3VPNv6. Using SRv6 EVPN L3VPNv6 is recommended.

## Slide 42: SRv6 Solution: IGP & BGP Design
IGP design: Use the existing network design for IGP planning. The existing IPv4 network does not need to be redesigned. It is advised to use IS-IS and enable IPv6 (IS-IS for IPv6).
BGP design: BGP focuses on the control and advertisement of routes. After an IGP is deployed, PEs need to establish BGP peer relationships to advertise service routes through different address families.
PE1
PE2
PE4
PE3
RR1
RR2
P1
P2
EBGP
IBGP
BGP-based advertisement of service routes &
SRv6 locators/SRv6 SIDs
PE1
PE3
PE2
PE4
IS-IS for IPv6 (Level 2)
Loopback route
Locator route
IS-IS for IPv6 (single area)
BGP EPE/BGP-LS
Overview
DC
WAN
Other Systems
Campus Network
Notes: Loopback routes and SRv6 locator routes need to be advertised in an IGP domain. Loopback routes are used for network management or BGP peer relationship establishment. Locator routes are used to guide the forwarding of data traffic over SRv6 tunnels in an IGP domain.
BGP Egress Peer Engineering (EPE) is used to allocate SRv6 SIDs to BGP peers between ASs in inter-AS scenarios.

## Slide 43: SRv6 Solution: Layer 3 IPv6 Services (1)
Implementing EVPN L3VPNv6 over SRv6 involves establishing SRv6 paths, advertising VPN routes, and forwarding data.
PE1
P1
PE2
CE1
CE2
MP-BGP
SRv6
2. Advertises locator routes.
3. Advertises IPv6 routes.
4. Learns VPN instance IPv6 routes and generates EVPN routes.
5. Advertises EVPN routes carrying VPN SIDs.
6. Receives the EVPN routes and generates VPN instance IPv6 routes carrying SRv6 VPN SIDs.
7. Advertises the IPv6 routes.
Service establishment procedure (SRv6 BE)
A user configures SRv6 and IPv6 VPN instances on PEs, and configures transit devices to support IPv6.
PE2 advertises an SRv6 locator route to PE1.
CE-to-PE route advertisement: CE2 advertises its IPv6 routes to PE2. Static routes, OSPFv3, IS-IS for IPv6, or BGP4+ can be used between CEs and PEs.
After learning the VPN route advertised by CE2, PE2 installs it in the IPv6 routing table of the corresponding VPN instance and converts it into an EVPN IP prefix route.
Inter-PE route advertisement: PE2 advertises an EVPN route to PE1 (BGP EVPN peer) through an update message carrying RT and SRv6 VPN SID attributes.
PE1 receives the EVPN route. If the next hop in the EVPN route is reachable and the route matches the BGP route import policy, PE1 performs a series of actions to determine whether to install the route in the IPv6 routing table of the corresponding EVPN instance. These actions include route leaking, route recursion to an SRv6 path, and route selection. The VPN route is associated with an SRv6 VPN SID when being delivered.
PE-to-CE route advertisement: CE1 can learn VPN routes from PE1 in multiple modes, including static routing, OSPFv3, IS-IS for IPv6, and BGP4+. The route exchange between CE1 and PE1 is similar to that between CE2 and PE2.
VPN1
VPN1
IPv6
IPv6
1. Configures an IPv6 VPN instance.
1. Configures an IPv6 VPN instance.
Overview
DC
WAN
Other Systems
Campus Network

## Slide 44: SRv6 Solution: Layer 3 IPv6 Services (2)
Implementing EVPN L3VPNv6 over SRv6 involves establishing SRv6 paths, advertising VPN routes, and forwarding data.
PE1
P1
PE2
CE1
CE2
MP-BGP
SRv6
Advertises IS-IS routes.
2002:1::/64
VPN1
VPN1
IPv6
IPv6
Advertises IS-IS routes.
2002:1::/64
Advertises IPv6 routes.
2100::1/128
Advertises IPv6 routes.
2100::1/128
Advertises the EVPN route 2100::1/128, with the next hop being PE2, and the VPN SID being 2002:1::D100.
SA=2001:1::1
DA=2002:1::D100
SA=2200::1
DA=2100::1
Payload
SA=2200::1
DA=2100::1
Payload
SA=2001:1::1
DA=2002:1::D100
SA=2200::1
DA=2100::1
Payload
SA=2200::1
DA=2100::1
Payload
Route advertisement
Data forwarding
Configured locator: 2002:1::/64
Generated End SID: 2002:1::1
Configured VPN SID: 2002:1::D100
Configured locator: 2001:1::/64
Generated End SID: 2001:1::1
Configured End.DT6 SID: 2002:1::D100
Local SID Table generation
Locator
Opcode
2100::1/128
Note: SRv6 BE route advertisement and data forwarding are used as an example.
2200::1/128
Overview
DC
WAN
Other Systems
Campus Network
Notes: Route advertisement:
  PE2 generates an End SID based on the configured SRv6 locator.
  PE2 advertises the locator route 2002:1::/64 corresponding to the specified End SID to PE1 through an IGP. PE1 installs the route to its IPv6 routing table.
  A VPN End.DT6 SID 2002:1::D100 within the locator range is configured on PE2, which then generates Local SID Table.
  After receiving the VPN IPv6 route advertised by CE2, PE2 converts it into an EVPN IP prefix route and advertises it to PE1 through the BGP EVPN peer relationship. The route carries an SRv6 VPN SID — VPN End.DT6 SID 2002:1::D100.
  After receiving the EVPN route, PE1 leaks it to the IPv6 routing table of the corresponding VPN instance, converts it into a common IPv6 route, and advertises it to CE1.

## Slide 45
Notes: Data forwarding:
  CE1 sends a common IPv6 packet to PE1.
  After receiving the packet through the interface bound to a VPN instance, PE1 searches the IPv6 routing table of the corresponding VPN instance for a matching IPv6 prefix and finds the associated SRv6 VPN SID and next hop. Then, the device directly uses the SRv6 VPN SID 2002:1::D100 as the destination address and encapsulates the packet into an IPv6 one.
  PE1 finds the route 2002:1::/64 based on the longest match rule and forwards the packet to the P device over the shortest path.
  Similarly, the P device finds the route 2002:1::/64 based on the longest match rule and forwards the packet to PE2 over the shortest path.
  PE2 searches Local SID Table based on 2002:1::D100 and finds a matching End.DT6 SID. According to the instruction bound to the SID, PE2 removes the IPv6 header and searches the IPv6 routing table of the VPN instance corresponding to the End.DT6 SID for packet forwarding.
Note:
  End SID: identifies an SRv6 destination node on the network.
  VPN SID: identifies a VPN service.
  End.DT6: decapsulates a packet and searches a specified IPv6 routing table for packet forwarding.

## Slide 46: Campus Network IPv6 Evolution Overview
Overall IPv6 evolution roadmap for campus networks:
Phase 1 (IPv6 dual stack)
IPv4 for management networks
Dual stack for campus egress networks
Underlay IPv4 + overlay dual stack for campus networks
Phase 2 (IPv6 dual stack)
Dual stack for management networks
Dual stack for campus egress networks
Underlay IPv6 + overlay dual stack for campus networks
Phase 3 (IPv6 only)
IPv6 only for management networks
IPv6 only for campus egress networks
IPv6 only for campus networks
After an enterprise campus network completes dual-stack reconstruction, terminals on the network can access both IPv4 and IPv6 services.
Generally, the IPv6 capabilities of live network devices need to be evaluated during the reconstruction of existing networks. If their IPv6 capabilities do not meet the reconstruction requirements, these devices need to be replaced or upgraded.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Campus networks mainly involve large- and medium-sized office campuses, small-sized branch office campuses, and industrial production campuses. There are three scenarios for intra-campus mutual access: mutual access between internal office systems, Internet access, and mutual access between production systems.
  During dual-stack reconstruction for large- and medium-sized office campus networks, the original IPv4 network architecture and configurations are retained, and IPv6 configurations and IPv6-related support systems are added.
  In large- and medium-sized virtualized campus scenarios, underlay IPv4 + overlay VXLAN dual stack can be used to evolve VXLAN to IPv6 based on live network device capabilities.
  When a small office campus network is upgraded to IPv4/IPv6 dual-stack, services from terminals inside the campus to the enterprise HQ need to be transmitted through WAN dual-stack channels. Considering the campus network scale and WAN line leasing solution, we can determine which option to choose based on live network conditions:
    In the scenario where only a single Internet private line is leased for backhaul, the campus egress generally connects to the intranet over an IPsec tunnel. One of the following solutions can be used: dual-stack traffic over IPsec6, dual-stack traffic over IPsec4, and dual-stack traffic over GRE over IPsec6/4.

## Slide 47
Notes:     In the scenario where only an MPLS VPN private line is leased for backhaul, the MPLS VPN private line needs to be upgraded to support IPv4/IPv6 dual-stack connections. Campus egress routes can flexibly interwork with carriers' MPLS VPN private lines using BGP, IGP, or static routes.
    In the scenario where multiple backhaul modes (such as MPLS VPN and Internet private lines) are available, the SD-WAN technology can be used to flexibly select routes for IPv4 and IPv6 traffic. If campus WAN links are not upgraded, IPv6 service traffic can be encapsulated using IPv4 GRE and then transmitted over the SD-WAN.

## Slide 48: Phase 1 IPv6 Evolution Strategy for Traditional Campus Networks
DC
Internet
Evolution roadmap
Controller deployment: Deploy an SDN controller in the DC.
New core switch deployment: Deploy new core switches in the campus core equipment room and connect them to other network areas. The connections are consistent with those of the existing core switches. In addition, establish temporary links to the legacy core network for service cutover.
Basic route configuration: Configure basic routes for future service interworking on core switches and interconnection devices.
Building-by-building reconstruction: Perform IPv6 and SDN reconstruction in a building. Connect aggregation switches in the building to new core switches and deliver services through SDN to devices in this building. Meanwhile, add routes to this building on the new core switches and interconnection devices.
After all buildings are reconstructed, the entire network has evolved to IPv6 and SDN.
Building 1 (IPv4)
Building 2 (IPv4)
Building 2 (IPv6)
VXLAN
(IPv6)
IPv6 and SDN reconstruction
NAT64
New core
Note: The IPv6 devices in the new building and IPv4 devices in the old building need to communicate through NAT64 devices in the DC.
Service interworking between the network after IPv6 reconstruction and network before IPv6 reconstruction
Overview
DC
WAN
Other Systems
Campus Network
Notes: Phase 1 evolution strategy: Perform IPv6 and SDN evolution concurrently to achieve two objectives at one time.
  Overall solution roadmap: Create a core network that supports SDN and IPv6 network virtualization, and connect the core network to the campus egress network. Reconstruct the existing network building by building (aggregation + access) and connect the network to the new core network. Use the SDN controller for automated deployment in reconstructed buildings.
  Solution advantages: Operations are simple, the deployment pace is controllable, and the impact on live network services is minimized.

## Slide 49: IPv6 Reconstruction for Large- and Medium-Sized Traditional Campus Networks (1)
Network management zone
Internet
WAN
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
AC
DHCPv6 relay
DHCPv6 server
L3
L2
Address allocation:
Before considering the address allocation solution, you must determine the address types and planning for the enterprise campus network. A large enterprise group has a large number of users and a large network scale and can apply for GUA PI addresses independently. Therefore, it is recommended that the enterprise group apply for GUA PI addresses independently and allocate campus addresses uniformly.
Campus terminals can obtain IPv6 addresses through DHCPv6, SLAAC, or manual configuration. Generally, the DHCPv6 or SLAAC solution can be used to obtain addresses for wired terminals. If the DHCPv6 solution uses the centralized server mode, DHCPv6 relay needs to be deployed gradually to relay DHCPv6 packets. Android terminals do not support DHCPv6 and must use the SLAAC solution to obtain addresses.
Overview
DC
WAN
Other Systems
Campus Network
Notes: Large- and medium-sized traditional campus networks generally use Layer 3 IP forwarding and use Layer 2 VLANs to isolate broadcast domains. If Layer 3 isolation is required, ACLs can be deployed. For external services such as Internet access and enterprise WAN interconnection, intra-campus support systems include AAA authentication servers and DHCP servers. During dual-stack reconstruction for large- and medium-sized traditional campus networks, the original IPv4 network architecture and configurations are retained, and IPv6 configurations and IPv6-related support systems are added.
GUA: global unicast address
The PI address space is a block of IPv6 addresses assigned by a regional Internet registry to enterprises.

## Slide 50: IPv6 Reconstruction for Large- and Medium-Sized Traditional Campus Networks (2)
Network management zone
Internet
WAN
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
AC
OSPFv3
area 0
OSPFv3
area 1
OSPFv3
area 2
L3
L2
Interconnection between internal networks:
The Layer 3 network of the campus network is upgraded and reconstructed to support IPv4/IPv6 dual-stack communication. Considering the scale of the enterprise campus network and the general user habits of the original IPv4 network, OSPFv3 is enabled as the IGP, and OSPFv3 area settings are the same as those of OSPFv2 to ensure Layer 3 route reachability in the campus network.
An enterprise campus network can communicate with a WAN in multiple modes. For example, static default routes, IGP routes, or BGP routes can be used for interconnection.
The interconnection mode between the campus network and WAN depends on factors such as the capabilities of the campus egress devices, the number of campus egress paths, and campus egress traffic. This scenario is not closely related to IPv6. Therefore, it is recommended that the IPv4 network interconnection policy still be used.
Static routing/IGP
/BGP
Static routing/
BGP
IGP-based internal
default route advertisement
Overview
DC
WAN
Other Systems
Campus Network
Notes: Interconnection with external networks:
  For example, if the campus network IPv6 addresses are PI addresses independently applied for, static routes can be used for interconnection with external networks and IGPs can be used to advertise default routes on the internal network. Carrier networks advertise specific routes to the campus network, and default egress routes are configured on the campus network.
  If multiple egresses are involved, BGP can be used for interconnection with external networks and IGPs can be used to advertise default routes on the internal network. The campus network internally advertises default egress routes to ensure that internal service packets can reach egress routers. The egress routers connect to the Internet using BGP to implement optimal path selection and load balancing.

## Slide 51: IPv6 Reconstruction for Large- and Medium-Sized Virtualized Campus Networks (1)
Currently, the virtualized network solution (VXLAN) is deployed on some large- and medium-sized campus networks to meet the requirements of these networks, such as one network for multiple purposes and fast, automated service provisioning.
VXLAN underlay IPv4 + overlay dual stack can be used for the IPv6 evolution of virtualized campus networks. The horizontal traffic between networks in an enterprise campus is light. The centralized gateway mode is generally used in the virtualized network VXLAN solution. Therefore, the centralized gateway mode is used in the following examples.
Internet
WAN
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
AC
DHCPv6
relay
DHCPv6 server
L3
L2
Address allocation:
There are three network address allocation modes: DHCPv6, SLAAC, and manual configuration. If the DHCPv6 or SLAAC mode is used for automatic address allocation, the virtualized network design is different from that of the traditional network.
In DHCPv6 address allocation mode, the DHCPv6 server needs to be deployed in centralized mode, and DHCPv6 relay needs to be enabled on the VBDIF interface serving as the centralized VXLAN IPv6 gateway to relay DHCPv6 packets. Android terminals do not support DHCPv6 and must use the SLAAC solution to obtain addresses.
In SLAAC address allocation mode, RA parameters need to be configured on the centralized gateway, so that the centralized gateway pushes RA messages carrying address prefixes and DNS information to terminals.
Overview
DC
WAN
Other Systems
Campus Network

## Slide 52: IPv6 Reconstruction for Large- and Medium-Sized Virtualized Campus Networks (2)
Internet
WAN
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
AC
Fabric
VXLAN underlay IPv4 (OSPFv2)
Overlay dual stack
L3
L2
If enterprise campus networks use the virtualization solution (VXLAN underlay IPv4 + overlay IPv4), we only need to enable IPv6 at the overlay layer and configure the dual-stack capability in the egress zone to upgrade these networks to support IPv6.
OSPFv2/
OSPFv3
area 0
Centralized gateway
Static routing/IGP
/BGP
Static routing/BGP
IGP-based default route advertisement
VXLAN underlay IPv4 + overlay dual stack
AP
AP
Overview
DC
WAN
Other Systems
Campus Network
Notes: Service forwarding:
  The overlay IPv6 design is similar to the original overlay IPv4 design. The underlay configuration from the access layer to the core layer remains unchanged. The VXLAN control plane uses BGP EVPN, and core switches are configured as RRs. Enable IPv6 on the centralized gateway and configure an IPv6 address for the VBDIF interface to ensure Layer 2 IPv6 communication.
  Edge nodes on the access side can associate forwarded packets with overlay BDs based on interface VLANs, enabling terminals to be assigned to different gateway areas. In VXLAN Layer 3 forwarding, terminal packets are first advertised to the centralized gateway, and horizontal and vertical traffic are forwarded by the gateway in a unified manner.
  For design details about internal network interconnection and external network interconnection involved in the network egress zone, see the traditional campus network solution.
Access authentication:
  Edge nodes on the campus network provide access for dual-stack users. Single authentication and dual-stack service policy association needs to be implemented for dual-stack users. This helps prevent dual-stack terminals from undergoing two separate authentications when accessing IPv4 and IPv6 services.
  A campus network with VXLAN underlay IPv4 + overlay dual stack must support various authentication modes (such as 802.1x, Portal, and MAC address authentication) for IPv6 users, so that authentication schemes can be implemented flexibly based on user terminals (such as Portal authentication for guest terminals and 802.1x authentication for internal office terminals). The deployment of network authentication points, policy enforcement points, and access points in the IPv6 solution is consistent with that in the original IPv4 solution. The authentication server uses a unified controller to provide authentication policy services.

## Slide 53: WLAN IPv6 Access
IPv6 evolution and upgrade of campus networks involves WLAN reconstruction. Currently, WLANs in large- and medium-sized single campus networks usually use AC+ FIT AP networking. The IPv6 upgrade and reconstruction of WLANs mainly focus on the management between ACs and APs and the address obtaining modes of access wireless terminals. Other WLAN designs are not affected by IPv6 upgrade and reconstruction.
Internet
WAN
Egress zone
Core layer
Aggregation layer
Access layer
Terminal layer
AC
L3
L2
CAPWAP6 tunnel
As shown in the figure, an AC connects to core switches in bypass mode, and APs connect to access switches. The APs are configured with multiple SSIDs for IPv6 single-stack users using internal office terminals and guest terminals to access the wireless network. The authentication point is on the AC.
AP
Overview
DC
WAN
Other Systems
Campus Network
Notes: Wireless terminal access solution:
  The core switches or AC functions as the gateway for wireless access of office terminals. The SLAAC hybrid solution can be used to configure IPv6 addresses for terminals, and 802.1x authentication can be used.
  Different VLANs are configured for guest SSIDs. The core switches or AC functions as the gateway for wireless access of guest terminals. The SLAAC hybrid solution is used to allocate IPv6 addresses. Portal authentication is recommended.
AP management solution:
  The CAPWAP tunnel supports both IPv4 and IPv6. However, only IPv4 or IPv6 can be selected at one time. That is, the AC can manage APs only in either IPv4 or IPv6 mode. The default mode is IPv4.
  APs can go online in either IPv4 or IPv6 mode. That is, an AP can obtain only one IP address. The AC's IP address is manually configured. The AC can use DHCPv6 or SLAAC to assign IP addresses to APs.
Note: You can run the capwap ipv6 enable command to enable the IPv6 function for the CAPWAP tunnel.

## Slide 54: IPv6 Reconstruction of Other Related Systems (1)
The key to internal application system reconstruction is to adjust address-related modules.
IPv6 reconstruction of application systems mainly involves the network layer.
The network layer is used to transparently transmit data between two end systems and is a channel for communication between application systems.
Application programs connect to application processes and network protocol stacks through sockets to implement binding between application programs and network protocol interfaces.
IPv4 application
IPv4/IPv6 application
TCP
TCP
UDP
UDP
IPv4
IPv4
IPv6
Ethernet
Ethernet
Protocol
0x0800
Protocol
0x86DD
Protocol
0x0800
IPv4 only
IPv4/IPv6 dual stack
General suggestions on IPv6 reconstruction of application systems:
Deploy an IPv6-capable DNS system and add AAAA records to the system. All service systems identify remote hosts by domain names instead of using IP addresses as host identifiers. Check whether applications can correctly parse the AAAA records of URLs.
Check whether the application system directly uses IP addresses. Ensure that IP addresses are used only as addresses, not as user IDs or key service attributes, and ensure that services are independent of IP address types.
Check the socket communication interface. Ensure that this interface has shifted from an IPv4-oriented programming interface to one that supports IPv4&IPv6 compatibility. Use IPv6-oriented functions, macros, and libraries to check whether the code for verifying IP address validity needs to be modified.
Overview
DC
WAN
Other Systems
Campus Network

## Slide 55: IPv6 Reconstruction of Other Related Systems (2)
NMS
The management and control planes of the NMS can still use the IPv4 solution. IPv6 reconstruction can be performed after network-wide reconstruction.
Currently, iMaster NCE does not require special licenses for delivering IPv6 services. Currently, mainstream functions such as user management and free mobility support both IPv4 and IPv6 services.
DNS server
The DNS servers provided by BIND and Microsoft are mainstream DNS servers in the market.
BIND9 and later versions support IPv6 address resolution. Microsoft Server 2003 and later versions support IPv6.
If the current service version is later than the preceding version, we only need to add IPv6 address resolution through simple configurations.
Note: If Internet domain name resolution is involved, ensure that the upper-level DNS server provides the IPv6 capability before the reconstruction.
Portal web system
The web server mainly provides the Internet browsing service, which is the most widely used service on the Internet. Currently, the commonly used web server software includes Apache, Nginx, and Microsoft IIS.
Apache provides IPv6 support since version 2.0.11.
Nginx 0.7.36 and later versions support IPv6.
Microsoft's IIS service has supported IPv6 since IIS 6.0 was released in 2003.
If the current service version is later than the preceding version, we can enable the IPv6 service through simple configurations.
Check whether the code for using IP addresses for communication exists in the portal's front-end implementation. If yes, change the IP addresses to URLs or absolute addresses.
Server operating system
The common operating systems of servers include Linux, Unix, and Windows Server.
If the operating system does not meet the version requirements (supporting IPv6), upgrade the operating system.
Database system
Common database systems support IPv6 as follows. If the current version of a database system is earlier than the following, we need to upgrade it.
MySQL 5.7.17, Microsoft SQL Server 2016, Oracle Database 12.1.0.2.0, MariaDB 10.2.9, IBM DB2 10.5, FileMaker Pro 16.0.2.205, FileMaker Server 16.0.1.185, PostgreSQL 10, IBM Informix Dynamic Server (IDS) 11.5, Sybase OpenSwitch 15.1, etc.
Overview
DC
WAN
Other Systems
Campus Network
Notes: NMS IPv6 reconstruction:
  The NMS is not user-oriented and requires only a small number of IP addresses. Therefore, IPv4 addresses can still be reserved for internal communication, and IPv6 addresses are only optional.
  Through reconstruction, the NMS can also provide the following functions:
    Identifies and manages various IPv6 address types.
    Supports DNS resolution monitoring in IPv6.
    Collects performance, resource, and fault data of IPv6 and dual-stack devices, and provides functions such as performance management, resource management, and fault management and analysis for these devices.
    Associates IPv4 with IPv6 for dual-stack devices, so that the resource, performance, and fault data of these devices can be smoothly associated with historical data.
    Accesses the IPv6 MIBs of devices through IPv4-based SNMP and obtains IPv6 configuration, traffic, and other information from the IPv6 MIBs.
IPv6 reconstruction for server operating systems:
  Common Linux versions that support IPv6 are as follows (IPv6 installed by default):
    Fedora 13, Red Hat Enterprise Linux 6, Ubuntu 12.04, Oracle Solaris 10, SUSE Linux Enterprise Server 11, etc.
  Windows Server supports IPv6 as follows:
    Windows Server 2003 supports IPv6, but IPv6 is not installed by default and needs to be manually installed.
    Windows Server 2008 and later versions have IPv6 installed by default.

## Slide 56
(Multiple-answer question) Which of the following deployment solutions may be used during WAN IPv6 evolution? ( )
  Dual stack
  6VPE
  SRv6
  VXLAN underlay IPv4 + overlay dual stack
(True or false) IPE technologies include network programming, network slicing, deterministic networking, in-band flow measurement, new multicast, and application awareness. ( )
  True
  False
Notes: ABC
A

## Slide 57
Enterprise networks generally involve DCNs, WANs, and campus networks. IPv6 evolution needs to take into consideration the overall capability upgrade and coordination of applications, terminals, and networks to ensure that the user experience of existing services is not affected during IPv6 evolution. IPv6 solution design must ensure smooth and continuous network evolution. During the solution design, consider using the optimal IPv6 technologies to build next-generation IPv6 informatization infrastructure and facilitate sustainable service development.
This course describes the evolution trends of IPv6 networks in scenarios such as DCs, WANs, and campus networks and the technical application of IPE technologies.