## Slide 1
Datacom
General
V1.0
Chen Can/WX934766
2020.05.25
Li Xianzhi/00354681
New
He Junjian/WX580230
2021.08.17
Li Xianzhi/00354681
Update
Yu Sheng/WX1092303
2021.10.16
Lu Yueyue/WX445705
Update

## Slide 2: SSH Fundamentals and Practice

## Slide 3
To achieve efficient O&M and enhance agility amid increasingly complex service requirements and network architecture, network automation is gaining momentum and ever evolving. Currently, Secure Shell (SSH) is the most common method used by engineers to log in to devices for remote management. As such, engineers are expected to learn about and use an automation tool to implement SSH remote login, simulate man-machine interaction with O&M personnel, and automatically transfer files.
In this course, we will use the Python Paramiko module to write automation scripts to implement SSH-based preliminary network automation.

## Slide 4
On completion of this course, you will be able to:
  Describe the basic concepts and working principles of SSH.
  Understand the concept of Paramiko.
  Master the composition and common methods of Paramiko.
  Grasp the common methods for implementing Paramiko.

## Slide 5
Introduction to SSH
  Overview of SSH
  Working Principles of SSH
  Overview of Paramiko
Paramiko Component Architecture
SSH Practices

## Slide 6: Overview of SSH
Secure Shell (SSH) is a protocol for secure remote login and other secure network services over an insecure network.
SSH consists of the following sub-protocols: SSH transport layer protocol, SSH user authentication protocol, and SSH connection protocol.
User Authentication Protocol
SSH transport layer protocol
SSH user authentication protocol
SSH connection protocol
Negotiates the version and algorithm and exchanges keys.
Authenticates users (password and key).
Establishes a session connection.

## Slide 7: SSH Transport Layer Protocol
SSH transport layer protocol is a secure transport protocol. The SSH transport layer is usually established over TCP/IP connections. It can also be established over any other reliable data flow.
The SSH transport layer protocol negotiates all key exchange algorithms, public key algorithms, symmetric encryption algorithms, and message authentication algorithms.
Algorithm Type | Function | Name
Key exchange algorithm | Generates session keys. | diffie-hellman-group14-sha1, diffie-hellman-group1-sha1, etc.
Public key algorithm | Performs digital signature and user authentication. | ssh-rsa, ssh-dss, etc.
Symmetric encryption algorithm | Encrypts sessions. | aes128-ctr, 3des-cbc, etc.
Message authentication algorithm | Verifies data integrity. | hmac-sha1, hmac-md5, etc.
Notes: Perfect Forward Secrecy (PFS) is a property of secure communication protocols. PFS was proposed by Christoph G. Gunther in 1990. PFS is essentially defined as the cryptographic property of a key-establishment protocol in which the compromise of a session key or long-term private key after a given session does not cause the compromise of any earlier session. PFS ensures that any future disclosure of passwords or keys cannot be used to decrypt any communications sessions recorded in the past, even if the attacker proactively intervenes.
The SSH transport layer protocol uses the Diffie-Hellman key exchange algorithm to implement PFS.
For details, see section 9.3.7 "Forward Secrecy" in RFC 4251 (https://www.ietf.org/rfc/rfc4251.txt).

## Slide 8: SSH User Authentication Protocol
The SSH user authentication protocol authenticates the client-side user to the server. It runs over the transport layer protocol.
The SSH user authentication protocol provides two authentication methods: password authentication and public key authentication.
  Password authentication: The client uses the user name and password for authentication before successfully logging in to the server.
  Public key authentication: The server decrypts the digital signature of the client by using a public key.
Client
Server
User name + Password
Password authentication
Public key authentication
Client
Server
Digital signature
Notes: A public key is used to decrypt information to ensure message authenticity and integrity. Therefore, the receiver knows that the information comes from someone who has a private key. The encrypted information is called a digital signature. The public key is in the form of a digital certificate.
When the SSH user authentication protocol is started, it receives a session ID from the SSH transport layer protocol. The session ID uniquely identifies a session and is a part of the digital signature to indicate the ownership of the private key.

## Slide 9: SSH Connection Protocol
The SSH connection protocol multiplexes several logical channels into a single encrypted tunnel. It provides interactive login sessions, remote execution of commands, forwarded TCP/IP connections, and forwarded X11 connections.
The SSH connection protocol runs on top of the SSH transport layer protocol and user authentication protocol.
Session channel
TCP/IP forwarding channel
X11 channel
SSH connection
SFTP channel
Notes: A TCP/IP connection can forward network data of other TCP ports through SSH channels, ensuring security.
Data of Telnet, SMTP, IMAP, and other TCP/IP-based insecure protocols can be forwarded through SSH, which prevents the transmission of user names, passwords, and privacy information in plaintext and therefore enhances security. In addition, if the firewall restricts the use of some network ports but allows the SSH connection, communication can be implemented through the SSH TCP/IP connection.
In X11, X refers to the X protocol, and 11 is the eleventh version of the X protocol. The Linux graphical user interface (GUI) is based on the X protocol at the bottom layer. When remote interaction with graphical applications on the Linux server is required, a method for enhancing communication security is to use SSH to display the GUI on the local client through the X11 tunnel.
A session is a remote execution of a program. A program can be a shell, an application, a system command, or some built-in subsystems. Multiple session channels can be active at the same time. An interactive login session can be implemented using the invoke_shell() method, and the remote command can be implemented using the exec_command() method, which will be described in detail later.

## Slide 10
Introduction to SSH
  Overview of SSH
  Working Principles of SSH
  Overview of Paramiko
Paramiko Component Architecture
SSH Practices

## Slide 11: Working Principles of SSH
In the entire communication process, to implement a secure SSH connection, the server and client go through the following five phases:
  Version negotiation phase: Two versions of SSH are available: SSH Version 1 (SSHv1) and SSH Version 2 (SSHv2). The server and client determine the version to be used through negotiation.
  Algorithm negotiation phase: SSH supports multiple encryption algorithms. The server and client negotiate the encryption algorithm to be used based on the algorithms that they support.
  Key exchange phase: A session key is generated by using a key exchange algorithm. The subsequent sessions between the server and client are encrypted by using the session key.
  User authentication phase: The SSH client sends an authentication request to the server, and the server authenticates the SSH client.
  Session interaction phase: After the authentication succeeds, the server and client exchange information.
Version negotiation
1
Algorithm negotiation
2
Key exchange
3
Client
Server
User authentication
4
Session interaction
5
Transport Layer Protocol
User Authentication Protocol
Connection Protocol

## Slide 12: Version Negotiation Phase
The client and server exchange SSH version negotiation packets to determine whether to use SSHv1 or SSHv2.
Client
Server
Server protocol: SSH-2.0--
Send an SSH version negotiation packet.
Establish a TCP connection.
Three-way TCP handshake
Client protocol: ssh-2.0-paramiko_2.7.1
Send an SSH version negotiation packet.
Protocol | SSH-<Major protocol version number> .<Secondary version number>-<Software version number>
2
3
1
Notes: Port 22 is enabled on the server, waiting for the client to connect. The client initiates a TCP connection to the server. The two parties complete the handshake and establish a connection. The client sends a packet to the server. The packet contains the version field, in the format of Major version number.Secondary version number-Software version number. After receiving the packet, the server parses it to obtain the protocol version number. If the protocol version number of the client is earlier than that of the server and the server supports the earlier version of the client, the server uses the protocol version number of the client. Otherwise, the server uses its own protocol version number.

## Slide 13: Algorithm Negotiation Phase
The client and the server exchange a list of algorithms that they support. The list includes specific names of the four types of supported algorithms.
Server:Key Exchange Init
Send a list of supported algorithms.
Client:Key Exchange Init
Send a list of supported algorithms.
The server searches its algorithm list for matching algorithms. If a match is found for each type of algorithm, the next phase starts. Otherwise, the connection is disconnected.
Key exchange algorithm | diffie-hellman-group1-sha1,diffie-hellman-group-exchange-sha256,diffie-hellman-group14-sha1
Public key algorithm | ecdsa-sha2-nistp384,ssh-rsa,ssh-dss
Symmetric encryption algorithm | aes192-ctr,aes256-ctr,aes128-ctr
Message authentication algorithm | hmac-sha2-512,hmac-sha1,hmac-md5
Server
1
2
3
Client
Key exchange algorithm | diffie-hellman-group14-sha1,ecdh-sha2-nistp521
Public key algorithm | ssh-dss,ssh-rsa,ecdsa-sha2-nistp521
Symmetric encryption algorithm | aes128-ctr,3des-cbc,aes256-ctr
Message authentication algorithm | hmac-sha2-512, hmac-sha1,hmac-md5
Notes: The algorithm negotiation process is as follows: The server obtains the first algorithm from the algorithm list of the client and searches its own algorithm list for the same algorithm. If the same algorithm is found, the negotiation succeeds, and the server continues to negotiate the algorithm of the next type. Otherwise, the server searches its own algorithm list for the next algorithm in the client's algorithm list until a match is found.

## Slide 14: Key Exchange Phase
Based on the key exchange algorithm, the server and client dynamically generate a session key for subsequent session encryption. The session key cannot be intercepted by a third party, enhancing security and reliability.
The client generates a random private key Xc, calculates a public key Yc, and sends the public key Yc to the server.
The server generates a random private key Xs, calculates the public key Ys, and sends the public key Ys to the client.
The client calculates the session key based on the public key Ys and private key Xc.
The server calculates the session key based on the public key Yc and the private key Xs.
Subsequent packets are encrypted based on the session key, and the encryption algorithm is the symmetric encryption algorithm determined in the algorithm negotiation phase.
The server and client agree on the prime numbers p and g.
Client
Server
Data
p, g
Xc
Yc
Data
p, g
Xc
Ys
Session Key
1
2
3
4
Data
p, g
Xs
Yc
Session Key
Data
p, g
Xs
Ys
Notes: The client and the server first agree on two public prime numbers p and g.
The client and server each randomly generate a private key Xc and Xs, respectively.
The client and server each calculate their own public key Yc and Ys, respectively.
The client and server exchange their own public key.
The client and server calculate the session key for encryption based on the public and private keys.
The Diffie-Hellman key exchange algorithm is used for key exchange, which is based on the mathematical discrete logarithm and is not described in this course. During key exchange, the private keys Xc and Xs are not transferred and, due to the difficulty in computing discrete logarithms, they cannot be decrypted by other users even if p, g, Yc, and Ys are obtained. This ensures the confidentiality of the session keys.
Note that the public and private keys generated in this phase are used only to generate session keys and are irrelevant to subsequent user authentication. After the key exchange phase is complete, all subsequent packets are encrypted based on the session keys.

## Slide 15: User Authentication Phase: Password Authentication
There are two user authentication modes: password authentication and public key authentication.
During password authentication, the client sends an authentication request carrying the user name and password, and the server authenticates the received user information against the local user information.
Initiate an authentication request.
SSH_MSG_USERAUTH_REQUEST
Compare the user name and password with those saved locally. If they are the same, an authentication success message is returned.
SSH_MSG_USERAUTH_SUCCESS
Client
Server
User name | testuser
Authentication method | password
Password | testpwd
1
2

## Slide 16: User Authentication Phase: Public Key Authentication
During public key authentication, a client sends an authentication request carrying a digital signature, and the server decrypts the digital signature based on the public key to implement authentication.
Decrypt the digital signature using the locally stored public key, and check the correctness of the public key and digital signature provided by the client. If they are correct, an authentication success message is returned.
Initiate an authentication request.
Manually generate the public and private keys.
Manually copy the public key to the server.
Client
Server
User name | testuser
Authentication method | publickey
Public key algorithm | ssh-rsa/ssh-dss …
Public key | ssh-rsa AAAAB3NzaC1yc2EA…
Digital signature | Contains data such as the user name, session ID, public key algorithm, and public key.
SSH_MSG_USERAUTH_REQUEST
SSH_MSG_USERAUTH_SUCCESS
1
2
Notes: The digital signature is encrypted by client’s private key. To see the content, we need public key to decrypt it.

## Slide 17: Session Interaction Phase
After the user is authenticated, the client sends a request to the server for establishing a channel to transmit data.
Initiate a request to establish a session channel.
SSH_MSG_CHANNEL_OPEN
Check whether the channel type is supported. If so, a message is returned, indicating that the session channel is successfully created.
SSH_MSG_CHANNEL_OPEN_CONFIRMATION
Transmit data.
Client
Server
1
2
The data is encrypted by using a symmetric encryption algorithm based on session keys.
Notes: The channel types include session, x11, forwarded-tcpip, and direct-tcpip.
For details, see section 4.9.1 "Connection Protocol Channel Types" in RFC4250 at https://www.ietf.org/rfc/rfc4250.txt.
Different ssh logical channels can multiplex one ssh session.

## Slide 18
Introduction to SSH
  Overview of SSH
  Working Principles of SSH
  Overview of Paramiko
Paramiko Component Architecture
SSH Practices

## Slide 19: Overview of Paramiko
Paramiko is a Python module that implements the SSHv2 protocol. It supports password authentication and public key authentication and implements functions such as secure remote command execution and file transfer.
Engineers can compile Python code based on the Paramiko module to implement SSH functions.
SSH server
SSH client
SSH protocol interaction
Paramiko Script
Notes: In HCIA courses, we learned how to use the telnetlib module for Telnet remote connections. In the production environment, the more secure Paramiko module is recommended for SSH remote connections.

## Slide 20
Introduction to SSH
Paramiko Component Architecture
  Paramiko Component Architecture
  Transport Class and Its Methods
  Key Handling Class and Its Methods
  SFTPClient Class and Its Methods
  SSHClient Class and Its Methods
SSH Practices

## Slide 21: Paramiko Component Architecture
The following figure shows the components of the Paramiko module. SSHClient and SFTPClient are its most commonly used classes, which provide the SSH and SFTP functions, respectively.
This course describes the methods of the Transport, key handling, SSHClient, and SFTPClient classes.
Packetizer
Message
SSHClient
Channel
Transport
Paramiko
Key handling
Host keys
SSH agents
SFTPClient
Key-related
classes
Common protocol classes

## Slide 22: Common Paramiko Classes
Channel: This class is used to create a secure channel over the SSH transport layer.
Message: An SSH message is a stream of bytes that encodes some combinations of strings, integers, bools, and infinite-precision integers (known in Python as longs).
Packetizer: This class is used for packet handling.
Transport: This class is used to create a transport session object over an existing socket or socket-like object.
SFTPClient: This class creates an SFTP session connection through an open SSH transport session and performs remote file operations.
SSHClient: This class is an advanced representation of a session with the SSH server. This class integrates the Transport, Channel, and SFTPClient classes.
Packetizer
Message
SSHClient
Channel
Transport
SFTPClient
Common protocol classes
Notes: The Channel class provides methods for executing commands, requesting X11 sessions, sending data, and opening interactive sessions. Generally, these common methods from the Channel class have been packaged in the SSHClient class.
The Message class provides methods for writing bytes to a stream and extracting bytes.
The Packetizer class provides methods for checking handshakes and obtaining channel IDs.
The Transport class provides methods such as public key authentication, private key authentication, and channel opening.
The SSHClient class provides methods for establishing connections and opening interactive sessions.
The SFTPClient class provides methods such as file upload and download.

## Slide 23: Key-Related Classes of the Paramiko Module
SSH Agent: This class is used for the SSH agent.
Host keys: This class is related to the OpenSSH known_hosts file and is used to create a host keys object.
Key handling: This class is used to create instances of the corresponding key type, for example, RSA keys and DSS (DSA) keys.
Key-related classes
Key handling
Host keys
SSH agents
Notes: OpenSSH is a free open-source implementation of the SSH protocol. It provides server programs and client tools. OpenSSH is integrated in all Linux operating systems. OpenSSH records the public key of each computer that a user has accessed in ~/.ssh/known_hosts. When the same computer is accessed next time, OpenSSH checks the public key. If the public keys are different, OpenSSH generates a warning to prevent man-in-the-middle attacks.

## Slide 24: Process of Using Paramiko
Instantiate the SSH session channel
Configure password authentication
Set up an SSH session connection
Configure public key authentication
Send related instructions
Close the session channel
Transport class
tran = paramiko.Transport(('192.168.56.100',22))
Key handling class
key=paramiko.RSAKey.from_private_key_file(r'C:\Users\exampleuser\.ssh\id_rsa')
Transport class
tran.connect(username=‘client’, pkey=key)
SFTPClient class
sftp = paramiko.SFTPClient.from_transport(tran)
sftp.get(remote_path, local_path)
Transport class
tran.close()
Notes: This course describes methods of four classes: Transport, key handling, SSHClient, and SFTPClient.
This process uses the Paramiko SFTP session as an example. Because the SSHClient class integrates the Transport, Channel, and SFTPClient classes, the preceding methods can be implemented by the SSHClient class. This is especially true for SSH sessions.

## Slide 25
Introduction to SSH
Paramiko Component Architecture
  Paramiko Component Architecture
  Transport Class and Its Methods
  Key Handling Class and Its Methods
  SFTPClient Class and Its Methods
  SSHClient Class and Its Methods
SSH Practices

## Slide 26: Transport Class and Its Methods
Transport class: An SSH transport connects to a stream (usually a socket) to negotiate and encrypt sessions and perform authentication. Channels can then be created based on the encrypted sessions. Multiple channels can be multiplexed in a single session connection (in fact, this is often the case, such as port forwarding).
The following is an example of the method:
tran = paramiko.Transport(('192.168.56.100', 22))
tran.connect(username=‘client’, password=‘test’)
Common Method | Function
Transport(sock) | Creates a Transport object and instantiates the SSH session channel.
connect(username=“,password=None,pkey=None) | Establishes an SSH session connection and uses a password or private key for identity authentication.
close() | Closes the session.
Notes: For ease of use, you can use an address (as a tuple) or a host string as the sock parameter. The host string is the host name with an optional port, separated by a colon (:). If a port is transferred, it is converted to a tuple in the format (host name, port).

## Slide 27
Introduction to SSH
Paramiko Component Architecture
  Paramiko Component Architecture
  Transport Class and Its Methods
  Key Handling Class and Its Methods
  SFTPClient Class and Its Methods
  SSHClient Class and Its Methods
SSH Practices

## Slide 28: Key Handling Class and Its Methods
The key handling class is used to create instances of the corresponding key type, for example, RSA keys and DSS (DSA) keys. This class provides methods for reading and writing keys.
The following is an example of the method:
key=paramiko.RSAKey.from_private_key_file(r'C:\Users\exampleuser\.ssh\id_rsa')
Common Method | Function
RSAKey.from_private_key_file(filename) | Reads the RSA private key from a file to create a key object.
DSSKey.from_private_key_file(filename) | Reads the DSS private key from a file to create a key object.

## Slide 29
Introduction to SSH
Paramiko Component Architecture
  Paramiko Component Architecture
  Transport Class and Its Methods
  Key Handling Class and Its Methods
  SFTPClient Class and Its Methods
  SSHClient Class and Its Methods
SSH Practices

## Slide 30: SFTPClient Class and Its Methods
The SFTPClient class creates an SFTP session connection through an open SSH transport session and performs remote file operations.
The following is a typical example:
key=paramiko.RSAKey.from_private_key_file(r'C:\Users\exampleuser\.ssh\id_rsa')
tran = paramiko.Transport(('192.168.56.100', 22))
tran.connect(username=‘client’, pkey=key)
sftp = paramiko.SFTPClient.from_transport(tran) local_path=r'C:\Users\exampleuser\.ssh\vrptest.cfg'
remote_path= '/vrpcfg.cfg'
sftp.get(remote_path, local_path)
Common Method | Function
from_transport() | Creates an SFTP session connection through an open Transport session channel.
get() | Downloads a specified file.
put() | Uploads a specified file.

## Slide 31: Method from_transport
from_transport(): This method creates an SFTP client channel from the enabled Transport session channel.
The following is an example of the method:
    t = paramiko.Transport((‘192.168.56.100’, 22))
    sftp = paramiko.SFTPClient.from_transport(t)
Parameter | Description
T | An authenticated and enabled Transport session, in the format of (hostname,port).
windows_size | Size of the SFTP session window. This parameter is optional.
max_packet_size | Maximum size of the SFTP session window. This parameter is optional.

## Slide 32: Method get
get(): This method copies a remote file (specified by remotepath) from the SFTP server to the destination path (specified by localpath) on the local host. Any exception raised by operations will be passed through.
The following is an example of the method:
    local_path=r'C:\Users\exampleuser\.ssh\vrptest.cfg'
    remote_path= '/vrpcfg.cfg'
    sftp.get(remote_path, local_path)
Parameter | Description
remotepath | Remote file.
localpath | Destination path on the local host. The path must contain the file name. If only a directory is specified, an error may occur.

## Slide 33: Method put
put(): This method copies a local file (specified by localpath) from the local host to the destination path (specified by remotepath) on the SFTP server. Any exception raised by operations will be passed through.
The following is an example of the method:
    local_path=r'C:\Users\exampleuser\.ssh\vrptest.cfg'
    remote_path= '/vrpcfg.cfg'
    sftp.put(localpath, remotepath)
Parameter | Description
localpath | Local file.
remotepath | Destination path on the SFTP server. The path must contain the file name. If only a directory is specified, an error may occur.

## Slide 34
Introduction to SSH
Paramiko Component Architecture
  Paramiko Component Architecture
  Transport Class and Its Methods
  Key Handling Class and Its Methods
  SFTPClient Class and Its Methods
  SSHClient Class and Its Methods
SSH Practices

## Slide 35: SSHClient Class and Its Methods
The SSHClient class is an advanced representation of a session with an SSH server. This class contains the Transport, Channel, and SFTPClient classes for session channel establishment and authentication. The following is a typical example:
client=paramiko.client.SSHClient()
client.connect(hostname=192.168.56.100’,port=22,username=‘client’,password=‘123456’)
stdin,stdout,stderr=client.exec_command(‘ls –l’)
Common Method | Function
connect() | Connects to the remote server and implements authentication.
set_missing_host_key_policy() | Specifies a policy to be used when the connected server does not have a known host key.
load_system_host_key() | Loads the host key from the system file.
exec_command() | Runs Linux commands on the remote server.
invoke_shell() | Starts an interactive shell session on the remote server.
open_sftp() | Creates an SFTP channel in a session connection.
close() | Closes a connection.

## Slide 36: Method connect
connect(): This method is used to connect to a remote server and implement authentication.
The following is an example of the method:
    client.connect(hostname='192.168.56.100',port=22,username=‘client',key_filename='id_rsa')
    client.connect(hostname='192.168.56.100',port=22,username=‘client',password=‘123456')
Parameter | Description
hostname | Target host to be connected. Only this parameter is mandatory.
port | Specified port. The default value is 22.
username | User name for authentication. This parameter is left empty by default.
password | Password of the user to be authenticated. This parameter is left empty by default.
key_filename | Private key file name or list. This parameter is left empty by default.
pkey | Private key used for identity authentication.
... | ...

## Slide 37: Method set_missing_host_key_policy
set_missing_host_key_policy(): This method specifies a policy to be used when the connected server does not have a known host key.
The following is an example of the method:
  client.set_missing_host_key_policy(paramiko.client.AutoAddPolicy())
Parameter | Description
AutoAddPolicy | Automatically adds the host name and host key to the local HostKeys object, without depending on the configurations of the load_system_host_keys method. That is, when a new SSH connection is set up, you do not need to enter yes or no for confirmation.
WarningPolicy | Logs a Python-style warning for an unknown host key and accepts it. This method provides functions similar to AutoAddPolicy. The difference lies in that this method will display a message, indicating that the connection is a new connection.
RejectPolicy | Automatically rejects the unknown host name and key. This method depends on the configuration of the load_system_host_keys method. This is the default option.
Notes: OpenSSH records the public key of each computer that a user has accessed in ~/.ssh/known_hosts. When the same computer is accessed next time, OpenSSH checks the public key. If the public keys are different, OpenSSH generates a warning to prevent man-in-the-middle attacks. Generally, when a client connects to the SSH server for the first time, you need to enter Yes or No for confirmation.

## Slide 38: Method load_system_host_keys
load_system_host_keys(): This method loads the host key from the system file. If no parameter is specified, the system attempts to read the key from the known hosts file on the local host.
The following is an example of the method:
  client.load_system_host_keys()
Parameter | Description
filename | File name. This parameter is left empty by default.

## Slide 39: Method exec_command
exec_command(): This method is used to run Linux commands on a remote server.
The following is an example of the method:
    stdin,stdout,stderr=client.exec_command(‘ls –l’)

## Slide 40: Method invoke_shell
invoke_shell(): This method starts an interactive shell session based on the SSH session connection.
The following is an example of the method:
  cli = client.invoke_shell()

## Slide 41: Method open_sftp
open_sftp(): This method creates and opens an SFTP session on the SSH server.
The following is an example of the method:
  sftp=client.open_sftp()

## Slide 42
Introduction to SSH
Paramiko Component Architecture
SSH Practices
  Practices in SSH Python Scripts
  Practices in SFTP Python Scripts

## Slide 43: Case: Using SSH to Log In to a Device
Description:
  As shown in the figure below, after the STelnet server function is enabled on the switch that functions as the SSH server, the PC functioning as the SSH client can log in to the SSH server in password or RSA authentication mode.
  This case uses RSA user authentication as an example to describe how to configure a client so that it logs in to a server through SSH using the Paramiko module of Python.
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration
GE1/0/0
192.168.56.1
192.168.56.100
Stelnet Server
Stelnet Client

## Slide 44: Configuration Roadmap
Configuration on the server:
  Configure STelnet. Specially, configure a management IP address, enable the STelnet function, and configure the user interface.
  Configure users. Specially, create a local user and an SSH user, and configure the service type and authentication mode for the users.
  Configure a public key. Specially, add the public key generated by the client and allocate it to the user.
Configuration on the client:
  Generate a key pair. Specifically, generate a public key and a private key locally.
  Compile Python code.
  Verify the configuration.
GE1/0/0
192.168.56.1
192.168.56.100
Stelnet Server
Stelnet Client
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 45: Case: Configuring STelnet on the Server
Configure an IP address for the management network port on the server.
Enable STelnet on the server and configure the VTY user interface.
GE1/0/0
192.168.56.1
192.168.56.100
Stelnet Server
Stelnet Client
<HUAWEI>system-view immediately
[HUAWEI] sysname SSH Server
[SSH Server] interface GE 1/0/0
[SSH Server-GE1/0/0] ip add 192.168.56.100 24
[SSH Server-GE1/0/0] quit
[SSH Server] stelnet server enable
[SSH Server] user-interface vty 0 4
[SSH Server-ui-vty0-4] authentication-mode aaa
[SSH Server-ui-vty0-4] protocol inbound ssh
[SSH Server-ui-vty0-4] user privilege level 3
[SSH Server-ui-vty0-4] quit
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 46: Case: Configuring Users on the Server
Create a local user on the server, add the user to the administrator group, and configure the service type for the user.
GE1/0/0
192.168.56.1
192.168.56.100
Stelnet Server
Stelnet Client
[SSH Server] aaa
[SSH Server-aaa] local-user client password irreversible-cipher Huawei@123
[SSH Server-aaa] local-user client user-group manage-ug
[SSH Server-aaa] local-user client service-type ssh
[SSH Server-aaa] quit
[SSH Server] ssh user client
[SSH Server] ssh user client authentication-type rsa
[SSH Server] ssh user client service-type stelnet
Create an SSH user on the server and configure the authentication mode and service type for the user.
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 47: Case: Creating an RSA Key Pair on the Client
5. On the client, use Git Bash to create an RSA key pair (private key id_rsa and public key id_rsa.pub) and check the public key.
exampleuser@exampleuser MINGW64 ~
$ ssh-keygen -t rsa
Generating public/private rsa key pair.
Enter file in which to save the key (/c/Users/exampleuser/.ssh/id_rsa):
Enter passphrase (empty for no passphrase):
Enter same passphrase again:
Your identification has been saved in /c/Users/exampleuser/.ssh/id_rsa
Your public key has been saved in /c/Users/exampleuser/.ssh/id_rsa.pub
$ cat /c/Users/exampleuser/.ssh/id_rsa.pub
Check the public key. --
Generate an RSA public/private key pair --
Set the path for storing the key. (Press Enter to use the default path.) --
Enter the pass phrase. (Press Enter to use the default pass phrase.) --
Enter the pass phrase again. (Press Enter to use the default pass phrase.) --
Path for storing the private key file of the client. --
Path for storing the public key file of the client. --
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 48: Case: Configuring a Public Key on the Server
On the server, add the public key generated by the client and allocate it to the user.
[SSH Server] rsa peer-public-key rsa01 encoding-type openssh
[SSH Server-rsa-public-key] public-key-code begin
[SSH Server-rsa-public-key-rsa-key-code] ssh-rsa AAAAB3NzaC1yc2EAAAADAQABAAABgQDwLRx8MmuNs500dRemhFHdDbBmxco8Bp+wyqwaGuHJZBCjyFQV6AB+ezu5t0eWE3mw57IZfgmvR+MjBcliZv/x3l8oUMLcQKlKslYQDtvfUCZd+za1suXAPB/dyPKMhYPAzSDA7K+xqCWlmU3q06vxHEPLMv4A5IX54rKtBnK92fWjl9ACU+ak0ZlHxbKwOFn1tr0GJBazcInEs9DKGwkTTqJdu9+5hI5NxXTSbM3an53805ZbCU18xPy57g7MZC89vbdsag/uvQmFkLJ3arts/Om2R7fhR92EU/SNPmVy+qDEdwZEVdubdqJInW+8zzVkPGlnb2oH5hwH78Ksklbxb0fEfmGR0mS1ZAi3ZHUGcEEjuFZona3+5Z0Un2OPxfXwvoljVDusbYcugJHo9Ssurz05GzVuamQZlcO2JYY6FhtLUAImtXGQ80MpTjB0lcprkAZCib8agYOtVQNTZ7iB0g2EcBN9UTyMz7sh8RtrBDj445r+XPaDE8LmpDRKHMk=
[SSH Server-rsa-public-key-rsa-key-code] public-key-code end
[SSH Server-key-code] peer-public-key end
[SSH Server] ssh user client assign rsa-key rsa01
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration
Notes: For details about the commands, refer to the product documentation at https://support.huawei.com/enterprise/en/doc/EDOC1000097293/466984de?idPath=24030814|21432787|21430822|22318704|9794900.

## Slide 49: Case: Compiling Python Code on the Client
Compile and run Python code on the client to log in to the server through SSH.
import paramiko
import time
ssh = paramiko.SSHClient()
ssh.set_missing_host_key_policy(paramiko.AutoAddPolicy())
ssh.connect(hostname='192.168.56.100',port=22,username='client',key_filename=r'C:\Users\exampleuser\.ssh\id_rsa')
cli = ssh.invoke_shell()
cli.send('screen-length 0 temporary\n')
cli.send('display cu\n')
time.sleep(3)
dis_cu = cli.recv(999999).decode()
print(dis_cu)
ssh.close()
Import module --
Instantiate SSH objects. --
Allow connections to unknown hosts. --
Set up an SSH session connection. --
Open an interactive session. --
Send the command for canceling screen splitting. --
Send the command for displaying the current configuration. --
Set the pause duration to 3 seconds. --
Instantiate the received data. --
Print the command output. --
Close the SSH connection. --
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 50: Case: Verifying the Configuration on the Client
Run the code. The current configuration of the SSH server is displayed.
Info: The max number of VTY users is 5, the number of current VTY users online is 1, and total number of terminal users online is 2.
<SSH Server>screen-length 0 temporary
Info: The configuration takes effect on the current user terminal interface only.
<SSH Server>display cu
!Software Version V200R005C10SPC607B607
#
……
Enable STelnet on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 51
Introduction to SSH
Paramiko Component Architecture
SSH Practices
  Practices in SSH Python Scripts
  Practices in SFTP Python Scripts

## Slide 52: Case: Using SFTP to Upload and Download Files
Description:
  SSH File Transfer Protocol (SFTP) is a secure file transfer protocol based on SSH. SFTP not only provides all functions of FTP, but also has higher security and reliability.
  As shown in the figure below, after the SFTP server function is enabled on the switch that functions as the SFTP server, the PC functioning as a client can log in to the SFTP server in password or RSA authentication mode to upload or download files.
  This case uses RSA user authentication as an example to describe how to upload and download files on the client through SFTP using the Paramiko module of Python.
GE1/0/0
192.168.56.1
192.168.56.100
SFTP server
SFTP client
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 53: Configuration Roadmap
Configuration on the server:
  Configure SFTP. Specifically, configure the management IP address and enable SFTP on the device.
  Create a user. Specifically, create an SSH user and configure the service type, authentication mode, and SFTP path.
  Configure a public key. Specially, add the public key generated by the client and allocate it to the user.
  Verify the configuration. Specifically, check the uploaded files.
Configuration on the client:
  Generate a key pair. Specifically, generate a public key and a private key locally.
  Compile Python code.
  Verify the configuration. Specifically, check the downloaded files.
GE1/0/0
192.168.56.1
192.168.56.100
SFTP server
SFTP client
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 54: Case: Configuring SFTP and Users on the Server
Configure the management IP address for the SFTP server and enable the SFTP server function.
Create the SSH user client and configure the authentication type and service type for the user.
GE1/0/0
192.168.56.1
192.168.56.100
SFTP server
SFTP client
<HUAWEI>system-view immediately
[HUAWEI] sysname SFTP Server
[SFTP Server] interface GE 1/0/0
[SFTP Server-GE1/0/0] ip add 192.168.56.100 24
[SFTP Server-GE1/0/0] quit
[SFTP Server] sftp server enable
[SFTP Server] ssh user client
[SFTP Server] ssh user client authentication-type rsa
[SFTP Server] ssh user client service-type sftp
[SFTP Server] ssh user client sftp-directory cfcard:
[SFTP Server] ssh authorization-type default root
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 55: Case: Creating an RSA Key Pair on the Client
On the client, use Git Bash to create an RSA key pair (private key id_rsa and public key id_rsa.pub) and check the public key.
Generate an RSA public/private key pair. --
Set the path for storing the key. (Press Enter to use the default path.) --
Enter the pass phrase. (Press Enter to use the default pass phrase.) --
Enter the pass phrase again. (Press Enter to use the default pass phrase.) --
Path for storing the private key file of the client. --
Path for storing the public key file of the client. --
exampleuser@exampleuser MINGW64 ~
$ ssh-keygen -t rsa
Generating public/private rsa key pair.
Enter file in which to save the key (/c/Users/exampleuser/.ssh/id_rsa):
Enter passphrase (empty for no passphrase):
Enter same passphrase again:
Your identification has been saved in /c/Users/exampleuser/.ssh/id_rsa
Your public key has been saved in /c/Users/exampleuser/.ssh/id_rsa.pub
$ cat /c/Users/exampleuser/.ssh/id_rsa.pub
Check the public key. --
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 56: Case: Configuring a Public Key on the Server
On the server, add the public key generated by the client and allocate it to the user.
[SFTP Server] rsa peer-public-key rsa01 encoding-type openssh
[SFTP Server-rsa-public-key] public-key-code begin
[SFTP Server-rsa-public-key-rsa-key-code] ssh-rsa AAAAB3NzaC1yc2EAAAADAQABAAABgQDwLRx8MmuNs500dRemhFHdDbBmxco8Bp+wyqwaGuHJZBCjyFQV6AB+ezu5t0eWE3mw57IZfgmvR+MjBcliZv/x3l8oUMLcQKlKslYQDtvfUCZd+za1suXAPB/dyPKMhYPAzSDA7K+xqCWlmU3q06vxHEPLMv4A5IX54rKtBnK92fWjl9ACU+ak0ZlHxbKwOFn1tr0GJBazcInEs9DKGwkTTqJdu9+5hI5NxXTSbM3an53805ZbCU18xPy57g7MZC89vbdsag/uvQmFkLJ3arts/Om2R7fhR92EU/SNPmVy+qDEdwZEVdubdqJInW+8zzVkPGlnb2oH5hwH78Ksklbxb0fEfmGR0mS1ZAi3ZHUGcEEjuFZona3+5Z0Un2OPxfXwvoljVDusbYcugJHo9Ssurz05GzVuamQZlcO2JYY6FhtLUAImtXGQ80MpTjB0lcprkAZCib8agYOtVQNTZ7iB0g2EcBN9UTyMz7sh8RtrBDj445r+XPaDE8LmpDRKHMk=
[SFTP Server-rsa-public-key-rsa-key-code] public-key-code end
[SFTP Server-key-code] peer-public-key end
[SFTP Server] ssh user client assign rsa-key rsa01
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration
Notes: For details about the commands, refer to the product documentation at https://support.huawei.com/enterprise/en/doc/EDOC1000097293/466984de?idPath=24030814|21432787|21430822|22318704|9794900.

## Slide 57: Case: Compiling Python Code on the Client
Compile and run Python code on the client to log in to the server through SFTP and upload and download files.
import paramiko
key=paramiko.RSAKey.from_private_key_file(r'C:\Users\exampleuser\.ssh\id_rsa')
tran = paramiko.Transport(('192.168.56.100', 22))
tran.connect(username=‘client’, pkey=key)
sftp = paramiko.SFTPClient.from_transport(tran) local_path=r'C:\Users\exampleuser\.ssh\vrptest.cfg'
remote_path='/vrpcfg.cfg'
sftp.get(remote_path, local_path)
sftp.put(local_path,’/test.cfg’)
tran.close()
Import module.
Create an RSA key object.
Instantiate the session channel.
Set up an SSH session connection.
Set up an SFTP channel.
Set the local path.
Set the remote path.
Perform the download operation.
Perform the upload operation.
Close the session.
--
--
--
--
--
--
--
--
--
--
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 58: Case: Verifying the Configuration on the Server and Client
Run the code. The client successfully downloads the specified file to the local host.
Run the dir command on the server. The specified file is successfully uploaded to the server.
<SFTP Server>dir
Directory of cfcard:/
Idx Attr Size(Byte) FileName
5 -rw- 2,428 test.cfg
6 -rw- 2,493 vrpcfg.cfg
Configure SFTP on the device
Configure users
Configure the public key
Generate a key pair
Compile Python code
Verify the configuration

## Slide 59
(Multiple-answer question) Which of the following phases are involved in the SSH protocol? ( )
  Version negotiation phase
  Algorithm negotiation phase
  Key exchange phase
  User authentication phase
  Session interaction phase
Notes: ABCDE

## Slide 60
This course describes the concepts of Paramiko and SSH, and illustrates the working principles of SSH.
This course also describes the components and common methods of Paramiko. In the last part, this course uses example scripts of Python SSH and SFTP to show the use and practices of Paramiko methods, thereby implementing preliminary network automation based on SSH.
For more information, visit Paramiko's official website, read SSH RFC documents, and learn upper-layer SSH libraries such as Fabric. Fabric is developed based on Paramiko and is further encapsulated to improve SSH-based application deployment and system management efficiency.

## Slide 61
Paramiko official websites
  docs.paramiko.org/en/latest/index.html
  www.paramiko.com
SSH RFC documents
  https://tools.ietf.org/html/rfc4251.html
  https://tools.ietf.org/html/rfc4252.html
  https://tools.ietf.org/html/rfc4253.html
  https://tools.ietf.org/html/rfc4254.html
  Fabric official website
  https://fabric-chs.readthedocs.io/zh_CN/chs/tutorial.html