## Slide 1
Datacom
General
V1.0
Wei Jiongjian/WX935519
2020.06.16
Wan Changli/WX408647
New
He Junjian/WX580230
2021.08.24
Li Xianzhi/00354681
Update
Yu Sheng/WX1092303
2021.10.25
Lu Yueyue/WX445705
Update

## Slide 2: OPS Fundamentals and Practices

## Slide 3
A conventional network device is a closed system that provides fixed functions and services and is not dynamic or flexible. With the rapid development and popularization of networks, diversified and differentiated requirements emerge one after another. Conventional network devices cannot meet these requirements. Some customers require devices with specific openness so that they can develop their own functions and deploy proprietary management policies to implement automatic management and maintenance, lowering management costs.
Huawei has launched the open programmability system (OPS) to provide openness and programmability capabilities for network devices and enable users to perform secondary development, fully unleashing the potential of devices.
This course introduces the OPS, describes its principles and application scenarios, and provides a case.

## Slide 4
On completion of this course, you will be able to:
  Describe basic OPS concepts.
  Describe basic OPS functions.
  Understand the OPS working principles.
  Implement the basic OPS configuration.

## Slide 5
OPS Overview
OPS Fundamentals
OPS Application Scenarios
OPS Configuration Practices

## Slide 6: OPS Overview (1)
In the following scenarios:
  During network deployment, services need to be configured for a large number of devices after hardware installation.
  The network administrator wants devices to automatically take actions when alarms are generated.
  The network is disconnected when the network administrator wants to remotely deliver commands and periodically collect device information through compiled scripts.
Conventional network devices cannot effectively solve the problems in these scenarios and meet the requirements.
Administrator
Notes: Traditional network devices are relatively closed and cannot meet flexible and differentiated network management requirements.

## Slide 7: OPS Overview (2)
Huawei offers the OPS.
The OPS allows users and third-party developers to develop and deploy network management policies using open RESTful APIs. It implements rapid service expansion, automatic function deployment, and intelligent device management, helping reduce network operation and maintenance costs and simplify network operations.
RESTful API
System Capability
Administrator
Script
Notes: With the OPS, you can compile scripts based on their requirements and import the scripts to network devices for running, which is flexible and efficient.

## Slide 8
OPS Overview
OPS Fundamentals
OPS Application Scenarios
OPS Configuration Practices

## Slide 9: OPS Architecture
The OPS is developed on Huawei Versatile Routing Platform (VRP). It uses open RESTful APIs to work with VRP's management plane, control plane, and data plane, allowing for function expansion on a device.
The OPS provides managed objects (MOs) to open devices. Each MO is uniquely identified by a Uniform Resource Identifier (URI). The client can perform operations on objects using standard HTTP methods, such as GET, PUT, POST, and DELETE.
1998
RESTful API
Java
C/C++
……
Management Plane
Control Plane
Data Plane
python
Notes: The VRP system is developed by Huawei based on years of research and network application experience and its intellectual property rights is owned by Huawei.
Managed object (MO): an object that can be used to manage network devices by invoking RESTful APIs, such as CPU information, system information, and interface information.
Uniform Resource Identifier (URI): identifies a specific resource. In the OPS, URIs are used to identify MOs. For example, the URI of the CPU information is /devm/cpuInfos/cpuInfo, which uniquely identifies the CPU information.
Uniform resource locator (URL): A URL is a URI that can be used to present a resource and specify how to locate the resource, for example, http://www.ietf.org/rfc/rfc2396.txt and ftp://ftp.is.co.za/rfc/rfc1808.txt.
Huawei network devices that support the OPS provides a running environment for Python scripts. Scripts in Java and C/C++ languages are not supported.

## Slide 10: Introduction to RESTful APIs
Representational State Transfer (REST) is a style of software architecture. The design concepts and principles are as follows:
  All elements on networks can be abstracted as resources.
  Each resource has a unique resource ID. Operations on resources do not change the resource IDs.
  Standard methods are used to operate resources. The core operations are GET, PUT, POST and DELETE defined in HTTP.
  All operations are stateless.
RESTful API: application programming interfaces (APIs) that comply with the REST architecture.
The OPS defines a set of RESTful APIs and uses URIs to identify open MOs. You can access MOs using standard HTTP methods (GET, PUT, POST, and DELETE).
Notes: An API is a particular set of rules and specifications that are used for communication between software programs.
For more information about RESTful, see the HCIP Programming and Automation Course — RESTful Fundamentals and Practices.

## Slide 11: OPS RESTful API Interaction Example
With RESTful APIs defined by the OPS, you can write Python scripts to send HTTP requests to perform operations on MOs of network devices. Network devices will return HTTP response messages based on the operation results.
MOs:
CPU Information
System Information
Interface Information
Routing Information
…
HTTP Request
HTTP Response
Python
Script
Notes: The OPS allows you to compile Python scripts, install the scripts on network devices, and send HTTP requests when the scripts are running to manage network devices.

## Slide 12: Overview of HTTP
Hyper Text Transfer Protocol (HTTP) is the most widely used network transfer protocol on the Internet. It is used to transfer hypertext from the World Wide Web server to the local browser.
HTTP uses the client/server (C/S) architecture model and uses TCP/IP to transfer data, such as HTML files, image files, and query results. HTTP uses the TCP port 80 by default.
HTTP Request
HTTP Response
Web Server
Client
Notes: Currently, the implementation of RESTful APIs uses the HTTP standard specifications. Therefore, this section briefly describes HTTP.

## Slide 13: HTTP Packet Format (1)
HTTP packets are carried over TCP. The following figure shows the position of HTTP packets in TCP packets.
An HTTP packet (request message and response message) consists of the following:
  Start line: describes operations to be performed in a request packet and the execution result in a response packet.
  Header field: describes additional information about the request and response packets. For example, the header field Host in a request packet specifies the Internet host of the requested resource, and the header field Content-Type in the response packet header indicates the type of the content in the packet body.
  Body: The body of a request packet is the data to be sent by the client to the web server. The body of a response packet is the data to be returned by the web server to the client, such as HTML texts, images, and videos.
IP header
TCP header
TCP data
TCP packet segment
IP packet segment
HTTP packet

## Slide 14: HTTP Packet Format (2)
The syntax of HTTP packets is as follows:
 | Request Packet Format | Response Packet Format
Start line | <method> <request-URL> <version> | <version> <status-code> <reason-phrase>
Header field | <headers> | <headers>
Body | <entity-body> | <entity-body>
The request and response packets differ only in the syntax of the start line.
method: action that the client expects the server to perform on a resource. It is a single word, for example, GET or POST.
request-URL: path of the requested resource on the server.
version: HTTP version used by packets. The format is as follows: HTTP/<major version No.>.<minor version No.>.
status-code: HTTP status code, which indicates the execution result of a request operation. The status code is a three-digit number.
reason-phrase: reason phrase, which explains the status code in human-readable mode.
Notes: <headers> and <entity-body> are the header field and body of the packet on the previous page.

## Slide 15: HTTP Packet Format (3)
HTTP packet instance:
GET / HTTP/1.1
HTTP/1.1 200 OK
Request Packet
Response Packet
Start line
Header field
Body
The GET method is usually used to request the server to send a resource whose body is empty.
Host: www.example.com
User-Agent: Mozilla/5.0 (Windows NT 10.0; Win64; x64)
Accept: text/html,application/xhtml+xml
Accept-Language: zh-CN,zh;q=0.9
Date: Mon, YY-MM-DD 10:21:47 GMT
Server: VWebServer
Last-Modified: Mon, 15 Jun 2020 10:11:12 GMT
ETag: "e211-5a81ca574d000"
Accept-Ranges: bytes
Vary: Accept-Encoding
Content-Length: 13358
Content-Type: text/html
<HTML>
<HEAD>
<TITLE>Example Homepage</TITLE>
</HEAD>
<BODY>
<!– Body goes here -->
</BODY>
</HTML>
Notes: Header field:
  Host: contains host name and port number of the web server.
  User-Agent: contains information about the user agent originating the request.
  Accept: specifies response media types that are acceptable.
  Accept-Language: indicate the set of natural languages that are preferred in the response.
  Date: represents the date and time at which the message was originated.
  Server: contains information about the software used by the origin server to handle the request.
  Last-Modified: last modified date for the requested object.
  ETag: specifies an identifier for a specific version of a resource, often a message digest.
  Accept-Ranges: allows a server to indicate that it supports range requests for the target resource.
  Vary: describes what parts of a request message, aside from the method, Host header field, and request target, might influence the origin server's process for selecting and representing this response.
  Content-Length: indicates length of the response body in octets.
  Content-Type: indicates Multipurpose Internet Mail Extensions (MIME) type of content.
For details about the header fields, see RFC 2616.

## Slide 16: OPS RESTful API Description Example
The HTTP requests sent by a user must be constructed based on the RESTful APIs defined by the OPS. The API for obtaining system information is described as follows:
Request example including the HTTP header (XML format):
Response example including the HTTP header (XML format):
GET /system/systemInfo HTTP/1.1
Host: localhost
Accept-Encoding: identity
Content-Length: 66
Content-type: application/xml
Accept: application/xml
<?xml version="1.0" encoding="UTF-8"?>
<systemInfo>
</systemInfo>
HTTP/1.1 200 OK
Cache-Control: no-cache
Content-Type: application/xml
<?xml version="1.0" encoding="UTF-8"?> <systemInfo>
<sysName>HUAWEI</sysName>
<platformName>VRP</platformName>
<platformVer>v800r007c00</platformVer>
<productName>Device</productName>
<productVer>V800R007C00</productVer>
<patchVer></patchVer>
<esn>123456789</esn>
<mac>00e0-fc34-1234</mac>
</systemInfo>
Notes: The formats of the OPS RESTful API request and response packets are similar to those of the HTTP request and response packets described in the previous slide.
Extensible Markup Language (XML) is designed to transmit and store data.
Currently the OPS RESTful APIs use the XML format to transmit data. In a later version, the APIs can use the JavaScript Object Notation (JSON) format to transmit data. Therefore, the body of the OPS RESTful API request and response packets is in XML format.
You can download RESTful API Reference on the network device page of http://support.huawei.com.

## Slide 17: Usage of Python Scripts
Currently, the OPS RESTful APIs can be used only in the Embedded Running Environment (ERE). You can compile Python scripts based on OPS APIs and install them on the devices that provide a Python running system. When a Python script is running, an HTTP request is sent to the system to manage devices.
The following figure shows the Python script execution process.
Compile and upload a Python script
Install the Python script
Run the Python script
You can manually run a Python script using a command or configure the maintenance assistant function to run a Python script.
Only installed Python scripts can be run on a device.
Upload a Python script to a network device.
Notes: The maintenance assistant is a function of Huawei network devices. You can set the trigger conditions and the Python script to be executed when the conditions are met. The system monitors device running in real time. When the specified trigger condition is met, the network device system automatically executes the Python script to complete the actions defined in the script. For more information about the maintenance assistant, see the Huawei network device product documentation.

## Slide 18
OPS Overview
OPS Fundamentals
OPS Application Scenarios
OPS Configuration Practices

## Slide 19: Scenario 1: Automatic Deployment of Unconfigured Devices
The OPS can implement automatic deployment of unconfigured devices without the need of on-site installation, reducing labor costs and improving deployment efficiency.
DHCP
server
Script file server
Software and configuration
file server
DHCP relay
Switch
Download and run a Python script
Obtain the IP address, script server name, and script name
Download the Python script
Download the system software and configuration file
Notes: DHCP server: allocates the temporary IP address, default gateway, and script file server address to the device to be automatically deployed.
DHCP relay agent: forwards packets exchanged between the device to be automatically deployed and the DHCP server when they are located on different network segments.
Script file server: stores scripts (Python) required for automatic network device deployment. By running the script files, a network device can obtain information such as the IP address of the software and configuration file server, version file, and configuration file.
Software and configuration file server: stores system software, configuration files, and patch files required for automatic network device deployment.

## Slide 20: Scenario 2: Automatic Health Check
During conventional device health check, you need to log in to a device and run commands to check the hardware and service running status.
With the OPS function, a device can automatically run the health check commands, periodically collects health check results, and sends the results to a server for analysis. This function reduces maintenance workload. These commands are delivered through the Python scripts installed in the network device system instead of being remotely delivered. Therefore, you do not need to worry about network disconnection.
Automatically collects and sends device health information
Switch
Server
Notes: A Python script can be compiled to deliver commands. When the network is disconnected, the execution result is temporarily stored on the device. After the network is recovered, the execution result is transmitted to the server. Therefore, the impact of network disconnection can be mitigated.

## Slide 21: Scenario 3: Automatic Backup of Configuration Files
A network device subscribes to the configuration file saving events through the maintenance assistant. After the configuration is saved, the device automatically runs the Python script and sends its configuration file to the server for backup, reducing the manual backup workload.
Automatically back up the configuration file to the server
Switch
Server

## Slide 22
OPS Overview
OPS Fundamentals
OPS Application Scenarios
OPS Configuration Practices

## Slide 23: Configuration Roadmap
The configuration roadmap is as follows: The core is to compile Python scripts, which will be detailed later. For the operation modes and involved commands of the other three steps, see the following figure.
Upload a Python script
Install the Python script
Run the Python script
Compile the Python script
Through the maintenance assistant
Through the CLI (manual)
Command assistant
Script assistant
ops run python file-name
ops install file file-name
Upload the script to the network device through FTP.
For details about the maintenance assistant, see the product documentation.
Assume that a Python script has been compiled. Perform the following three steps to complete the configuration.

## Slide 24: Compiling a Python Script (1)
Python scripts are used to deliver HTTP requests to the system for management. Huawei provides Python script templates. You only need to search for RESTful APIs based on the functions to be implemented and modify code.
Example of a Python script template:
#!/usr/bin/env python
# -*- coding: utf-8 -*-
import traceback
import httplib
import string
class OPSConnection(object):
"""Make an OPS connection instance."""
#: an initialization class that creates an HTTP connection
def __init__(self, host, port = 80):
self.host = host
self.port = port
self.headers = {
(See the next slide for the rest of code.)
The import statement is used to import third-party modules required in the Python script template.
The OPSConnection class is used to invoke RESTful APIs. This class defines methods for establishing HTTP connections and does not need to be modified.

## Slide 25: Compiling a Python Script (2)
"Content-type": "text/xml",
"Accept": "text/xml"
}
self.conn = None
# Disable an HTTP connection.
def close(self):
"""Close the connection"""
self.conn.close()
# Create device resources.
def create(self, uri, req_data):
"""Create operation"""
ret = self.rest_call("POST", uri, req_data)
return ret
# Delete device resources.
def delete(self, uri, req_data):
"""Delete operation""“
ret = self.rest_call("DELETE", uri, req_data)
return ret
(See the next slide for the rest of code.)
Methods defined in the OPSConnection class:
  def _init_(): is an initialization method that creates an HTTP connection.
  def close(): shuts down an HTTP connection.
  def create(): creates device resources.
  def delete(): deletes device resources.

## Slide 26: Compiling a Python Script (3)
# Query device resources.
def get(self, uri, req_data = None):
"""Get operation"""
ret = self.rest_call("GET", uri, req_data)
return ret
# Modify device resources.
def set(self, uri, req_data):
"""Set operation"""
ret = self.rest_call("PUT", uri, req_data)
return ret
# Invoke classes internally.
def rest_call(self, method, uri, req_data):
"""REST call"""
print('|---------------------------------- request: ----------------------------------|')
print('%s %s HTTP/1.1\n' % (method, uri))
if req_data == None:
body = ""
else:
body = req_data
Methods defined in the OPSConnection class:
  def get(): queries device resources.
  def set(): modifies device resources.
  def rest_call(): indicates a class method that is invoked by a method mentioned above (create, delete, get, or set).
You do not need to modify the methods defined in the OPSConnection class.

## Slide 27: Compiling a Python Script (4)
print(body)
if self.conn:
self.conn.close()
self.conn = httplib.HTTPConnection(self.host, self.port)
self.conn.request(method, uri, body, self.headers)
response = self.conn.getresponse()
response.status = httplib.OK # stub code
ret = (response.status, response.reason, response.read())
print('|---------------------------------- response: ---------------------------------|')
print('HTTP/1.1 %s %s\n\n%s' % ret)
print('|------------------------------------------------------------------------------|')
return ret
# Define the function for obtaining system startup information.
def get_startup_info(ops_conn):
uri = "/cfg/startupInfos/startupInfo“
req_data = \
'''<?xml version="1.0" encoding="UTF-8"?>
You need to compile a method to invoke the RESTful API through an instance of the OPSConnection class to manage devices. For example, the def get_startup_info(ops_conn) method in this document is invoked to obtain system startup information. You can specify the method name.
uri = "/cfg/startupInfos/startupInfo" is the URI of the system startup information. Different MOs have different URIs. You need to change the URI as required.
The bold code needs to be modified based on the site requirements when you compile a Python script.

## Slide 28: Compiling a Python Script (5)
<startupInfo>
</startupInfo>
'''
# The response data of the system startup information is similar to the following:
'''
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply>
<data>
<cfg xmlns="http://www.huawei.com/netconf/vrp" format-version="1.0" content-version="1.0">
<startupInfos>
<startupInfo>
<position>6</position>
<nextStartupFile>flash:/vrpcfg.cfg</nextStartupFile>
<configedSysSoft>flash:/system-software.cc</configedSysSoft>
<curSysSoft>flash:/system-software.cc</curSysSoft>
<nextSysSoft>flash:/system-software.cc</nextSysSoft>
<curStartupFile>flash:/vrpcfg.cfg</curStartupFile>
<curPatchFile>NULL</curPatchFile>
<nextPatchFile>NULL</nextPatchFile>
</startupInfo>
You can obtain the values of uri and req_data from RESTful API Reference based on the site requirements.
The system startup information in this document is described in the RESTful API Reference as follows:
Operation | URI | Description
GET | /cfg/startupinfos/startupinfo | Obtain system startup information
Request example
<?xml version=“1.0” encoding=“UTF-8”?>
<startupInfo>
</startupInfo>

## Slide 29: Compiling a Python Script (6)
</startupInfos>
</cfg>
</data>
</rpc-reply>
''‘
# Execute a GET operation request.
ret, _, rsp_data = ops_conn.get(uri, req_data)
if ret != httplib.OK:
return None
return rsp_data
# main() function defines the operations to be performed during script running. You can modify the function according to service requirements.
def main():
"""The main function."""
host = "localhost"
try:
# Establish an HTTP connection.
ops_conn = OPSConnection(host)
# Invoke the function for obtaining system startup information.
According to the RESTful API Reference, the HTTP operation corresponding to the RESTful API for obtaining system startup information is GET. Therefore, the get method of the OPSConnection class instance is invoked.
You can change the get method to the create, delete, or set method of the OPSConnection class based on the device management function to be implemented.
req_data indicates the request content, and rsp_data indicates the response message after the network device performs the request operation.
In the main() method, host indicates the loop address. Currently, RESTful APIs can be invoked only inside the device, that is, the value is localhost.

## Slide 30: Compiling a Python Script (7)
rsp_data = get_startup_info(ops_conn)
# Disable an HTTP connection.
ops_conn.close()
return
except:
errinfo = traceback.format_exc()
print(errinfo)
return
if __name__ == "__main__":
main()
You can invoke the method compiled based on the RESTful API in the main() method, for example, the get_startup_info method in this document, to complete the desired function.
The main() method can flexibly implement various management functions of a network device by using various RESTful APIs and structures of Python such as loops and if-else.
The last line of the script indicates that the main() method is executed.

## Slide 31: Case: Obtaining CPU Information of a Device
Description: A network administrator compiles a Python script and uploads the script to a network device to obtain CPU information by using the OPS function of the device. The networking is as follows.
Network administrator
Network device
GE1/0/0
192.168.56.100
192.168.56.1
Python Script

## Slide 32: Compiling a Python Script (1)
Based on the function of obtaining device CPU information to be implemented, obtain the URI, request message, and response message by referring to the RESTful API Reference. The result is as follows.
URI information:
Request message:
Response message:
Operation | URI | Description
GET | /devm/cpuInfos/cpuInfo | Query a board's CPU usage
<?xml version=‘1.0’ encoding=‘UTF-8’?>
<cpuInfo>
<position></position>
<entIndex></entIdex>
<systemCpuUsage></systemCpuUsage>
<ovloadThreshold><ovloadTreshold>
<unovloadThreshold></unovloadThreshold>
</cpuInfo>
<?xml version=“1.0” encoding=“UTF-8”?>
<cpuInfo>
<position chassis=“1” slot=“17”>17</position>
<entIndex>17891329</entIndex>
<systemCpuUsage>5</systemCpuUsage>
<ovloadThreshold>95</ovloadThreshold>
<unovloadThreshold>75</unovloadThreshold>
</cpuInfo>
Notes: After knowing the format of the response message, you can parse the response message in the Python script. In this case, the response message is only displayed. You can try to parse the response message to implement more complex functions.

## Slide 33: Compiling a Python Script (2)
Modify the related code in the Python script template based on the URI and request content. Other code in the template does not need to be modified.
def get_cpu_info(ops_conn):
uri = “/devm/cpuInfos/cpuInfo“ #URI corresponding to the CPU information
req_data = \ #Set the content of the request for obtaining CPU information.
'''<?xml version='1.0' encoding='UTF-8'?>
<cpuInfo>
<position></position>
<entIndex></entIndex>
<systemCpuUsage></systemCpuUsage>
<ovloadThreshold></ovloadThreshold>
<unovloadThreshold></unovloadThreshold>
</cpuInfo>
'''
ret, _, rsp_data = ops_conn.get(uri, req_data) #Execute the get operation.
if ret != httplib.OK:
return None
return rsp_data
def main():
"""The main function.""“
host = "localhost"
try:
# Establish an HTTP connection.
ops_conn = OPSConnection(host)
# Invoke the function for obtaining CPU information.
rsp_data = get_cpu_info(ops_conn)
# Disable an HTTP connection.
ops_conn.close()
return
except:
errinfo = traceback.format_exc()
print(errinfo)
return
Define the get_cpu_info method.
Invoke the get_cpu_info method in the main method.

## Slide 34: Uploading a Python Script
After the Python script is compiled, save it as cpu_demo.py. The network administrator enables the FTP server on the local PC, and the network device functions as the FTP client to download the Python script.
<CE1>ftp 192.168.56.1 # Connect to the FTP server.
Trying 192.168.56.1 ...
Press CTRL + K to abort
Connected to 192.168.56.1.
220 WFTPD 2.0 service (by Texas Imperial Software) ready for new user
User(192.168.56.1:(none)):1 # Enter the user name.
331 Give me your password, please
Enter password: # Enter the password.
230 Logged in successfully
[ftp]get cpu_demo.py # Obtain the cpu_demo.py script file.
Warning: The file may not transfer correctly in ASCII mode.
500 Unidentified command SIZE cpu_demo.py
200 PORT command okay
150 "D:\FTPSERVER\cpu_demo.py" file ready to send (4605 bytes) in ASCII mode
..
226 Transfer finished successfully. # FTP transmission is complete.
FTP: 4605 byte(s) received in 1.135 second(s) 3.962Kbyte(s)/sec.
Notes: For details about how to enable the FTP server on the local PC, you can easily search the way from a search engine.

## Slide 35: Compiling a Python Script
After the Python script is uploaded, run the ops install file file-name command to install the script.
<CE1>ops install file cpu_demo.py # Install the Python script.
Verify the installation result.
<CE1>display ops script # Check the installed Python script.
--------------------------------------------------------------------------------
Index Size(Byte) Filename
--------------------------------------------------------------------------------
0 4605 cpu_demo.py
--------------------------------------------------------------------------------
The cpu_demo.py script has been successfully installed.

## Slide 36: Running the Python Script (1)
Run the ops run python file-name command to run the Python script.
<CE1>ops run python cpu_demo.py
|---------------------------------- request: ----------------------------------| # Content of the get operation
GET /devm/cpuInfos/cpuInfo HTTP/1.1
<?xml version='1.0' encoding='UTF-8'?>
<cpuInfo>
<position></position>
<entIndex></entIndex>
<systemCpuUsage></systemCpuUsage>
<ovloadThreshold></ovloadThreshold>
<unovloadThreshold></unovloadThreshold>
</cpuInfo>
|---------------------------------- response: ---------------------------------| # Content of the response message
HTTP/1.1 200 OK
<?xml version="1.0" encoding="UTF-8"?>
<rpc-reply>
<data>
<devm xmlns="http://www.huawei.com/netconf/vrp" format-version="1.0" content
-version="1.0">
(See the next slide for the rest of code.)

## Slide 37: Running the Python Script (2)
<cpuInfos> # Returned CPU information. In this case, the network device has
<cpuInfo> two cpus.
<position chassis=“1” slot=“1”>1</position> # position indicates the CPU position information.
<entIndex>16842753</entIndex> # entIndex indicates the CPU index information.
<systemCpuUsage>4</systemCpuUsage> # systemCpuUsage indicates the CPU usage.
<ovloadThreshold>90</ovloadThreshold> # ovloadThreshold indicates the CPU overload clearance threshold.
<unovloadThreshold>75</unovloadThreshold> # unovloadThreshold indicates the CPU non-overload threshold.
</cpuInfo>
<cpuInfo>
<position chassis="1" slot="17">17</position>
<entIndex>17891329</entIndex>
<systemCpuUsage>4</systemCpuUsage>
<ovloadThreshold>90</ovloadThreshold>
<unovloadThreshold>75</unovloadThreshold>
</cpuInfo>
</cpuInfos>
</devm>
</data>
</rpc-reply>
|------------------------------------------------------------------------------|

## Slide 38
(Multiple-answer question) The OPS function uses standard HTTP methods to access managed objects (MOs). Which of the following methods are supported? ( )
  GET
  PUT
  POST
  DELETE
Notes: ABCD

## Slide 39
The OPS is a unique function of Huawei network devices. It uses RESTful APIs and standard HTTP methods to access MOs on devices, helping users easily cope with various network O&M requirements.
Huawei provides Python script templates. You only need to search for RESTful APIs based on the functions to be implemented and modify code, which is easy to use.

## Slide 40
For more REST information, see the paper written by Dr. Roy Fielding.
  https://www.ics.uci.edu/~fielding/pubs/dissertation/top.htm
For more information about HTTP, see RFC 2616.
Python official website: https://www.python.org
RESTful API reference: https://support.huawei.com
Notes: The REST software architecture was first mentioned by Roy Fielding in his doctoral paper. Roy Fielding is one of the major authors of the HTTP specifications.