## Slide 1
Datacom
General
Chen Can/WX934766
2020.06.16
Li Xianzhi/00354681
New
He Junjian/WX580230
2021.08.24
Li Xianzhi/00354681
Update
Yu Sheng/WX1092303
2021.10.30
Wu Yue/WX291773
Update

## Slide 2: iMaster NCE-Campus Open API Introduction

## Slide 3
iMaster NCE-Campus is a next-generation SDN controller for enterprise campuses and is a core component of Huawei CloudCampus Solution.
iMaster NCE-Campus centrally manages and controls enterprise campuses and provides automatic deployment, security defense, and visualized O&M. It helps customers build service-centric dynamic scheduling capabilities of network services.
iMaster NCE-Campus provides standard-compliant open RESTful APIs for partners to develop innovative applications and continuously create value for enterprise customers.

## Slide 4
On completion of this course, you will be able to:
  Describe Huawei CloudCampus Solution.
  Describe main open APIs of iMaster NCE-Campus.
  Describe typical application scenarios of iMaster NCE-Campus.

## Slide 5
Solution Overview
Typical Scenarios and Open Capabilities
Openness and Cooperation Cases

## Slide 6: Huawei CloudCampus Solution
Open architecture: Pre-integration and easy integration
Pre-integrates the offerings from 30+ ecosystem partners and a feature database of 360+ terminals.
Provides 300+ APIs of four types for easy integration with third-party vendors.
Secure threat defense: Proactive threat defense and collaborative network protection.
Collects real-time data through security probes to implement network-wide security situation awareness.
Proactively identifies and handles security threats based on a security engine, with a threat identification rate of over 99%.
Ultra-broadband bearer: Scenario-specific innovations and ultra-broadband.
Ultra-broadband forwarding: 100GE core switches, ensuring non-blocking high-speed forwarding.
Ultra-broadband access: Industry's first commercial Wi-Fi 6 APs, successfully delivered to 10+ customers.
Scenario-specific innovations: All-scenario WLAN solutions ideal for coverage needs in different scenarios.
IoT: Convergence of IoT and Wi-Fi (Zigbee, RFID, BLE, and UWB).
Simplified deployment: Automated deployment and cloud-based architecture
Automation: automatic deployment based on the policy engine, with 50% higher efficiency.
Virtualization: VXLAN-based network virtualization, achieving one network for multiple purposes.
Cloudification: full-lifecycle cloud management service, deploying a branch network in minutes.
Intelligent O&M: Experience visibility and prediction-based optimization.
Data collection in seconds through telemetry, achieving user experience awareness throughout the journey.
85% fault identification rate based on expert experience and AI-based dynamic baseline exception detection.
Open
ecosystem
Smart
network
Virtual office
network
Virtual security protection network
Virtual production network
Network layer
Platform layer
Open API
Medium-sized campus
Small campus
Large-sized campus
Central AP
Telemetry/Context
NETCONF/YANG
Intent engine
Security engine
Policy engine
Analytics engine
Internet
Application layer
...
Electronic shelf label
Energy efficiency mgmt.
Asset mgmt.
Overlay
Underlay
Customer flow analysis
Ultra-broadband
connection
iMaster NCE
Campus Insight
Notes: iMaster NCE-Campus is Huawei's next-generation autonomous driving network management and control system for campus networks. It is a network automation and intelligent platform integrating manager, controller, analyzer, and AI functions. As such, this platform drives enterprise cloudification and digital transformation, and creates a shortcut to more automated network management and intelligent network O&M.

## Slide 7: CloudCampus Capability Openness Panorama
NETCONF/YANG/Telemetry/Syslog/SNMP/NetStream
Switch
Firewall
WLAN AP
AR
5
Network layer
Application layer
Industry focused
MSP
Authentication and accounting
Network management and monitoring
Log analysis
Business
Crowd profiling
Customer flow analysis
Electronic shelf label
Marketing reach
Education
Student health management
e-Schoolbag
AGV navigation
Asset management
Personnel management
Healthcare
Baby wristband
Asset management
Energy efficiency management
Personnel management
Office
...
Energy efficiency management
Asset
management
Solution platform layer (intent engine, policy engine, security engine, and analytics engine)
Platform layer
Value-added service API
Portal + RADIUS
Authorization API
Basic network API
Basic service API
O&M and monitoring API
Network configuration API
Policy service API
Third-party API
Terminal data API
Traffic data API
App data API
LBS API
Platform RSSI API
AP RSSI API
Bluetooth API
IoT API
Terminal layer
Mobile
IP phone
Tablet
Camera
Electronic shelf label
Asset tag
Smart wrist strap
Baby wristband
...
Partners
1
2
3
4
...
Manufacturing
IoT card
6
RFID
ZigBee
Bluetooth
30.0
Notes: Application layer: It focuses on mainstream scenarios and provides industry-wide applications. At this layer, network service data is shared, meeting value-added data and operation requirements.
Platform layer: It provides four types of APIs and supports industry-standard network interconnection protocols.
Network layer: It provides various open interfaces, such as NETCONF, YANG, and Telemetry, improving device manageability. APs are compatible with third-party IoT cards to implement IoT.
Terminal layer: It supports access of IoT terminals (such as ZigBee, RFID, and BLE), and access of wired and wireless terminals (such as mobile phones, IP phones, tablets, and cameras).

## Slide 8: Typical Cooperation Scenarios and Open APIs
NETCONF/YANG/Telemetry/Syslog/SNMP/NetStream
Switch
Firewall
WLAN AP
AR
5
Network layer
Platform layer
Value-added service API
Portal + RADIUS
Authorization API
Basic network API
Basic service API
O&M and monitoring API
Network configuration API
Policy service API
Third-party API
Terminal data API
Traffic data API
App data API
LBS API
Platform RSSI API
AP RSSI API
Bluetooth API
IoT API
IoT card
6
1
2
3
4
Typical cooperation scenarios
Energy efficiency management
Asset management
IoT-based positioning
Electronic shelf label
Authentication
and authorization
Smart IoT
Network
O&M
Crowd
profiling
Location-
based service
RFID
ZigBee
Bluetooth

## Slide 9
Solution Overview
Typical Scenarios and Open Capabilities
  Authentication and Authorization
  LBS
  Crowd Profiling
  Network O&M
  Smart IoT
Openness and Cooperation Cases

## Slide 10: Introduction to Authentication and Authorization
Authentication and authorization: A third-party authentication and authorization platform interworks with iMaster NCE-Campus to perform network access authentication and accounting for terminals that access Huawei intent-driven campus networks.
iMaster NCE-Campus provides two integration solutions for authentication and authorization using the third-party authentication and authorization platform. Tenants can select a solution based on the site requirements.
Integration Solution | Suggestions
Portal + RADIUS | iMaster NCE-Campus functions as a RADIUS client to interact with the third-party authentication and authorization platform for user authentication and authorization. Accounting is recommended in this solution.
Authorization API | After users are authenticated, the third-party authentication and authorization platform invokes the authorization API to instruct iMaster NCE-Campus to authorize the users. Accounting is not recommended in this solution.
Open API
Third-party authentication and authorization platform
Solution 1: Authorization API
Solution 2: Portal + RADIUS
Firewall
Switch
Cloud AP
Cloud AP
Authentication and authorization
Cloud AP
Notes: The tenant or MSP wants to use an existing or third-party authentication platform to authenticate user identities and authorize users for network access authentication through the web page (authentication portal). For example, an MSP provides a unified access authentication page for tenants.

## Slide 11: Interconnection Using the Authorization API
NAC device
802.11
Terminal
iMaster NCE-Campus
Third-party authentication and authorization platform
The terminal browser is redirected to the third-party portal server for the second time. (The URL of the key item carries the parameters of the first redirection, such as the MAC address of the terminal.)
The end user enters the user name and password to log in.
Delivers authorization to the device through the HACA channel.
Returns the authorization result.
The portal server sends the authentication result to the user through the HTTP page.
The authentication is successful. The user obtains the network access permission and downloads the app.
An HTTP/2 connection channel is set up between the device and controller.
The terminal browser is redirected to the iMaster NCE-Campus web UI.
The user access iMaster NCE-Campus.
Invokes the authorization API.
Invokes the API for querying authorization status.
The terminal browser accesses the third-party portal server page.
The terminal browser displays the login page.
The terminal accesses the network.
Brings the user offline
according to the third-party policy.
Invokes the user offline API.
Internet
Notes: To access the Internet, a user connects to the SSID of a Wi-Fi network and logs in to the portal pushed by a developer app. The developer app calls the authorization API of Huawei iMaster NCE-Campus to deliver the user's Wi-Fi access permission to the AP. The user then can access the Internet.
NAC is short for network access control.
Huawei Agile Cloud Authentication (HACA) is based on the mobile Internet protocol HTTP/2.

## Slide 12: Interconnection Using the Authorization API
Sample Code (Windows)
The API uses HTTPS and the port 18008.
This is a RESTful API, and Content-Type is application/json.
The following shows only a part of the API URL. For example, if the address of iMaster NCE-Campus is https://10.186.40.148:18008/, the complete URL of the authorization API is https://10.186.40.148:18008/controller/cloud/v2/northbound/accessuser/haca/authorization.
POST /controller/cloud/v2/northbound/accessuser/haca/authorization
{ "deviceMac":"AA:AA:AA:00:00:89", "deviceEsn":"AA50082935AAAA000088", "ssid":"YWFh", "policyName":"dfdsffd", "terminalIpV4":"10.11.11.11", "terminalMac":"ff-ff-ff-ff-ff-f1", "username":"liao", "nodeIp":"10.186.40.148", "apMac":"AA:AA:AA:00:00:89" }
STATUS CODE 200
{ "errcode": "", "errmsg": "", "psessionid": "846d65a4e1bb38c350a280f46e6d2f6ab0a688df7edbb72b77bc5d03e3926cd6" }
Response
Request
Notes: For more information about API-based authentication and authorization, visit https://devzone.huawei.com/cn/enterprise/campus/apiSolution.html.

## Slide 13: Interconnection Using Portal and RADIUS
If the authentication succeeds, the success page is displayed (pushed by the third-party portal server). If the authentication fails, the failure information page is displayed.
Instructs the AP to perform authorization.
The user page pushes the user name and password to iMaster NCE-Campus.
Instructs the user to push the user name and password to iMaster NCE-Campus.
Redirects the user to the third-party portal page. The user logs in to the page as prompted.
The user is redirected to the third-party portal page again.
Redirects the user to iMaster NCE-Campus.
The user is redirected to iMaster NCE-Campus.
Third-party portal server
Third-party RADIUS server
Client
AP
The user connects to a Wi-Fi network and opens a browser to access the Internet.
Initiates an access authentication request using RADIUS authentication packets.
Sends the accounting messages using RADIUS authentication packets.
Obtains page resources.
Accepts or rejects the access using RADIUS authentication packets.
Displays the page.
If authentication fails, a dialog box is popped up to display the failure information page.
iMaster NCE-Campus
Notes: For details about RADIUS-based authentication, visit https://devzone.huawei.com/cn/enterprise/campus/radiusSolution.html.

## Slide 14
Solution Overview
Typical Scenarios and Open Capabilities
  Authentication and Authorization
  LBS
  Crowd Profiling
  Network O&M
  Smart IoT
Openness and Cooperation Cases

## Slide 15: LBS Introduction
A location-based service (LBS) is deployed on a third-party LBS application platform and used to detect and locate terminals managed on Huawei intent-driven campus networks. The LBS provides the customer flow analysis, Wi-Fi marketing, and navigation based on the terminal locations.
Integration Solution | Suggestions
HTTPS + JSON | Applicable to the interconnection with an LBS system deployed based on software as a service (SaaS).
AP RSSI API | Applicable to the on-premise scenario.
Bluetooth API | Applicable to locating Bluetooth terminals and reporting terminal data.
Open API
LBS server
Method 1: HTTPS + JSON
Method 2: AP RSSI API
Firewall
Switch
Cloud AP
Cloud AP
Cloud AP
LBS
Method 3: Bluetooth API
BI
RSSI data
Application Scenario
Huawei provides location data of Wi-Fi and Bluetooth terminals to a third-party partner. The partner parses the location data and provides VAS applications, such as heat map, track tracing, and customer flow analysis, for end customers.
Notes: Location-based service (LBS) uses various locating technologies to obtain the current locations of devices and pushes information and basic service for these devices through mobile Internet.
iMaster NCE-Campus aggregates the terminal location data collected by cloud APs and periodically sends the data to the third-party LBS platform. After parsing and analyzing the location data with a series of algorithms, the LBS platform provides VASs, such as heatmap, tracking, and customer flow analysis, for customers.
Remarks: Partners need to meet related standards based on application scenarios, such as EU General Data Protection Regulation (GDPR).

## Slide 16: Data Reporting Process: HTTP + JSON Solution
Third-party platform (LBS server)
Client
AP
iMaster NCE-Campus
Generates the interconnection URL and secret.
Configures the interconnection URL and the secret field.
Generates the validator field.
Sets the validator field
Sends a GET request using HTTPS.
Returns the validator value.
Verifies the validator value.
Enables the data reporting function and delivers the configuration.
Collects terminal location data.
Reports RSSI data to iMaster NCE-Campus.
Reports RSSI data in JSON format to the third-party platform.
Preparation
Configuration
Send RSSI data to the third-party platform.
One-time
Periodic
Notes: iMaster NCE-Campus can directly report terminal location data to a third-party LBS platform. In this solution, iMaster NCE-Campus function as a relay agent.
For details about this process, see "Wi-Fi Terminal Location Practice in Huawei CloudCampus Solution" in the HCIP-Datacom-NCE Northbound Openness Lab Guide.

## Slide 17: Data Example: HTTP + JSON Solution
{
"data":[
{
"apMac":"4C:FA:CA:D8:23:A0",
"terminallist":[
{
"terminalMac":"88:19:08:F1:88:45",
"rssi":-68,
"timestamp":1557460789000
},
{
"terminalMac":"90:2E:1C:6A:2A:57",
"rssi":-57,
"timestamp":1557460789000
}
]
}
],
"secret":"Test@1234",
"type":"Aplocation"
}
secret: Used by a third-party LBS platform to verify the data sent by iMaster NCE-Campus. If the secret does not match that associated with the reported URL, the data is discarded. The value is generated by the third-party LBS platform, and is a string of 32 hexadecimal characters.
validator: Before sending data, iMaster NCE-Campus checks whether the validator returned by the peer end is correct. If the validator does not match that associated with the reported URL, iMaster NCE-Campus does not send Wi-Fi terminal location data to the third-party LBS platform.
Sample Code (Windows)
Notes: The validator value is in UUID format and is generated by iMaster NCE-Campus.
For more examples, visit https://developer.huaweicloud.com/techfield/network.html#CloudCampus.

## Slide 18: Data Reporting Process: AP RSSI API Solution
iMaster NCE-Campus allows WLAN APs to report terminal location data directly to a third-party LBS platform. iMaster NCE-Campus delivers the location reporting configuration to APs, and then the APs periodically send location packets to the third-party LBS platform.
Third-party LBS platform
Terminal
AP
iMaster NCE-Campus
1
Delivers the location reporting configuration to the AP.
2
Periodically sends location packets to the third-party LBS platform.
Notes: For more about the AP location reporting solution, see https://devzone.huawei.com/cn/enterprise/campus/lbsWiFiSolution.html#Wi-Fi Terminal Data Reporting Process.

## Slide 19: Data Reporting Process: Bluetooth API Solution
iMaster NCE-Campus allows WLAN APs to report terminal location data through Bluetooth Beacon packets. iMaster NCE-Campus delivers the Bluetooth-based terminal location configuration to APs. The APs then broadcast Bluetooth Beacon packets. After receiving the broadcast packets, terminals report their locations to the third-party LBS platform.
Third-party LBS platform
Terminal
AP
iMaster NCE-Campus
1
Delivers the Bluetooth-based terminal location configuration.
2
Broadcasts Bluetooth Beacon packets based on the delivered configuration.
3
Reports its location to the third-party LBS platform after receiving broadcast packets.
AP
Notes: For more about the Bluetooth API solution, see https://devzone.huawei.com/cn/enterprise/campus/lbsBluetoothSolution.html.

## Slide 20
Solution Overview
Typical Scenarios and Open Capabilities
  Authentication and Authorization
  LBS
  Crowd Profiling
  Network O&M
  Smart IoT
Openness and Cooperation Cases

## Slide 21: Crowd Profiling
Application Scenario
The business industry has the requirements for precision marketing. Direct marketing can tag specific people based on crowd profiles, and push target content to provide personalized services based on these tags. Crowd profiling requires two types of data: one is the data left online; the other type of data is left in brick-and-mortar stores (offline data), which can be collected using Wi-Fi probes and from network access data of customers.
Integration Solution | Suggestions
LBS API | Terminal location information is provided.
VAS API | Terminal login and logout information, network application information, and network traffic information are provided.
3rd-party service
Open API
Method 1: VAS API
Method 2: LBS API
Cloud AP
Cloud AP
Cloud AP
MSP
Crowd profiling: A third-party big data analysis platform analyzes the locations and status of terminals detected and managed on Huawei intent-driven campus networks to obtain the characteristics of crowd profiles in an area, so that target content can be pushed to the customers to provide personalized services.

## Slide 22: Invoking a VAS API
Device
iMaster NCE-Campus
Third-party network management and monitoring platform
The tenant administrator creates a northbound API administrator account.
The partner obtains the username and password, obtains the Token_id through postman, and carries the Token_id in the head of the invoked API to perform API-based authorization.
Adds a tenant administrator account.
Invokes the API.
Obtains the user status information.
Notes: For more about VAS APIs, visit https://devzone.huawei.com/cn/enterprise/campus/valueAddedApi.html.

## Slide 23
Solution Overview
Typical Scenarios and Open Capabilities
  Authentication and Authorization
  LBS
  Crowd Profiling
  Network O&M
  Smart IoT
Openness and Cooperation Cases

## Slide 24: Network O&M Overview
Network O&M: Third-party network management platforms (such as MSP-owned or mainstream network management and monitoring platforms) can manage or monitor devices managed by iMaster NCE-Campus.
Integration Solution | Suggestions
Network service API | Applicable to interconnection with various third-party private SaaS platforms.
APIs based on NETCONF, YANG, Telemetry, and SNMP | Applicable to interconnection with traditional network management platforms.
Application Scenario
MSPs and customers use their existing network management platform to manage or monitor devices that are supposed to be managed by iMaster NCE-Campus, such as creating tenant administrator accounts, managing devices, configuring networks for specified devices, and monitoring device status and alarms.
Currently, two methods are available to implement network O&M:
  Network service APIs: The third-party network management platform manages and monitors devices through RESTful APIs.
  Traditional device APIs based on NETCONF, YANG, Telemetry, and SNMP: Network management platforms can directly configure, manage, and maintain devices through these APIs.
3rd-party service
Open API
Method 1: VAS API
Method 2: APIs based on NETCONF, YANG, Telemetry, Syslog, SNMP, and NetStream
AP
MSP
Switch
Firewall
AR

## Slide 25: Interconnecting with a Third-Party Network Management and Monitoring Platform
Device
iMaster NCE-Campus
Third-party network management and monitoring platform
The tenant administrator creates a northbound API administrator account.
The partner obtains the account and password, obtains the Token_id through postman, and carries the Token_id in the head of the invoked API to perform API-based authorization.
Adds a tenant administrator account.
Configures an SSID.
Invokes the SSID configuration API.
Configures the SSID on iMaster NCE-Campus.
Delivers configurations.
Notes: For more basic network solutions, visit https://devzone.huawei.com/cn/enterprise/cloudcampus/quickStart.html#network.

## Slide 26
Solution Overview
Typical Scenarios and Open Capabilities
  Authentication and Authorization
  LBS
  Crowd Profiling
  Network O&M
  Smart IoT
Openness and Cooperation Cases

## Slide 27: Introduction to Smart IoT
Smart IoT: A third party expands an AP into an IoT base station through the open card capability of the AP to implement functions such as energy efficiency management, asset management, IoT locating, and electronic shelf label.
Application Scenario
When partners want to deploy IoT applications (such as electronic shelf label, IoT locating, energy efficiency management, and asset management), they can use Huawei's network infrastructure to provide IoT signal coverage (ZigBee, Bluetooth, and RFID), without the need to deploy a secondary IoT network.
Based on Huawei Cloud Campus Solution, partners can develop IoT cards and IoT service software on the cards to provide IoT services based on the network infrastructure.
  Huawei provides the network infrastructure, open AP hardware, and basic IoT card management and monitoring.
  Partners develop IoT cards, card software, and IoT service software.
Open API
Cloud AP
3rd-party service
Electronic shelf label
IoT locating
Energy efficiency management
Asset management

## Slide 28: Smart IoT: Open Cards
External card
Card
Card
USB port
IoT slot: allows IoT cards to be installed to provide extended functions.
AP4050DN-E
MT800
Built-in card
Notes: For more about the smart IoT solution, visit https://devzone.huawei.com/cn/enterprise/cloudcampus/quickStart.html#iot.

## Slide 29
Solution Overview
Typical Scenarios and Open Capabilities
Openness and Cooperation Cases

## Slide 30: Unified Cloud-based Wi-Fi Management in XX
XX provides Wi-Fi services over more than 800 cities and has 1.5 million users.
Challenges
Customer Benefits
Solution Implementation
iMaster NCE-Campus implements plug-and-play and fast deployment of devices and provides full-lifecycle cloud-based and centralized management, simplifying O&M. It provides open APIs to seamlessly interconnect with third-party authentication and accounting management platforms, implementing secure network management.
Cooperation Scenario and API
Authentication and authorization: Portal + RADIUS API
How to ensure Wi-Fi signal quality and user access experience in diversified tenant environments.
O&M for massive devices. A large number of tenants have devices scattered in difference places, resulting in high installation and O&M costs.
iMaster NCE-Campus
Cloud AP
...
3rd-party platform
Cloud AP
Background
High-quality Wi-Fi coverage
80% lower OPEX
Securer customer investment
Smooth
upgrade
Network
coverage
Cloud-based mgmt
Authentication
/Accounting
System management

## Slide 31: XX Builds the Future Business
Solution Implementation
Three-RF APs have an independent radio to provide LBS services for Wi-Fi terminals and tags. Bluetooth beacons in the underground garage achieve a locating precision of 1 m to 3 m. Open APIs connect to app platform to implement customer flow analysis, indoor navigation, and precision marketing, laying a solid foundation for operational decision-making.
Cooperation Scenario and API
LBS: AP RSSI API
XXX is a large city complex that integrates industry R&D, apartments, hotels, and businesses.
It is a landmark building group in XXX. Wireless networks are an important infrastructure.
Customer Benefits
Consumer experience: The customer requires high-density, high-quality wireless network access to provide precise indoor navigation in more than 160 stores and 30,000 parking spaces.
Smart operations: The customer wants to use big data analytics technology to describe consumer behavior and visualize staff locations in support of marketing and operational decision-making.
Authentication server
LDAP server
DHCP server
Map BI server
TAG location server
Terminal location server
AP4030TN
Access switch
Wi-Fi TAG
Aggregation switch
AC6605
Challenges
Background
High-quality Wi-Fi network
Big data-based precision marketing
Improved customers' shopping experience
Indoor
navigation
Network quality
Customer flow analysis

## Slide 32: Digital Transformation of the XX Supermarket
Network
management
platform
Dual-network convergence
Huawei AP4050DN-E provides built-in slots for IoT modules to converge Wi-Fi and IoT networks, achieving unified planning of the two networks.
Electronic shelf label
Electronic shelf labels interwork with the supermarket management system and customer's Enterprise Resource Planning (ERP) system to display prices in real-time and provide interactive functions such as code scanning, coupon claiming, and out-of-stock warning.
Wireless Internet service
Huawei AP4050DN-E helps build a high-quality wireless network for customers to scan QR codes for shopping or entertainment.
Cooperation Scenario and API
Smart IoT: IoT card
XX is a well-known chain supermarket in China.
One of China's top 500 enterprises and leading enterprise in China's national merchandising and agricultural industrialization
Challenges
Customer Benefits
Shopping experience: The customer wants to provide high-quality wireless network access to improve customers' shopping experience.
Manpower: The customer wants to reduce manpower and O&M costs, and improve the accuracy of supermarket services.
Background
Internet
AP4050DN-E
+ IoT card
Electronic shelf label
Store managemnt system
Electronic shelf label
AP4050DN-E
+ IoT card
Switch
WAC
30.0
30.0
Converged high-quality Wi-Fi
and IoT networks
ESL-based smart operation supermarket
Improved customers' shopping experience
Wireless
Internet
access
Converged
mgmt.
Smart operations

## Slide 33
(Multiple-answer question) Which of the following layers are available for openness on Huawei intent-driven campus networks? ( )
  Application layer
  Platform layer
  Network layer
  Terminal layer
Notes: ABCD

## Slide 34
This course describes the architecture, cooperation scenarios, and API packet structure involved in Huawei CloudCampus Solution to help readers understand the basic ecosystem openness capabilities of Huawei CloudCampus Solution and provide guides for interconnection between iMaster NCE and third-party applications based on these capabilities. It also helps MSPs, VAS application partners, and customers quickly implement system interconnection and service convergence, and helps customers and partners leverage network values.