## Slide 1
Course code
SD-WAN
V100R019C10
Chen Yong/00255710
2019-12-16
New
Wu Yue/WX291773
2020-09-04
Update

## Slide 2: SD-WAN Solution Technology Overview

## Slide 3
As digital transformation of enterprises steps into the cloud era and the software-defined networking (SDN) era is coming, software-defined WAN (SD-WAN) has become a next-generation solution for enterprise branch interconnection. It is widely deployed by enterprises due to its key features such as network-agnostic, intelligent traffic steering, zero touch provisioning (ZTP), and visualization.
There are many vendors in the SD-WAN field. According to statistics of Gartner, more than 60 vendors in the world have provided multi-layer SD-WAN solutions that support multiple business models by the end of 2019.
SD-WAN is deemed to be a next-generation enterprise branch interconnection solution by industry analysts, which has profound impact on and preliminarily replace existing traditional MPLS VPN services. In the future, SD-WAN will continue to develop and evolve rapidly oriented to emerging technologies and solutions such as cloud, 5G, XGSPON, artificial intelligence (AI), and blockchain.

## Slide 4
On completion of this course, you will be able to:
  Describe the architecture and components of Huawei SD-WAN Solution.
  Describe the basic implementation of Huawei SD-WAN Solution.
  Describe the functions and features of the customer-premises equipment (CPE).

## Slide 5
Architecture and Components of Huawei SD-WAN Solution
Huawei iMaster NCE-WAN
Implementation of Huawei SD-WAN Solution
Huawei SD-WAN CPEs

## Slide 6: Architecture of Huawei SD-WAN Solution
Service presentation layer: presents the SD-WAN service logic.
  Provides portal pages for carriers, MSPs, and large enterprises, on which SD-WAN services can be processed and enabled in an end-to-end manner.
  Allows customers to customize portal pages as needed through northbound open APIs of the SD-WAN controller (iMaster NCE-WAN).
Control layer: controls network layer devices. Typically, iMaster NCE-WAN is used to abstract the network model of an SD-WAN network, and pre-configure and automatically provision network services based on service templates.
Network layer: is the basic physical network of an enterprise WAN, which consists of physical and virtual devices including CPEs, virtual CPEs (vCPEs).
Network layer
Control layer
Service presentation layer
NETCONF/SSH
BGP/DTLS
HTTP/2
Orchestration
Control
RESTful API
Built-in Portal of the controller
Third-party BSS/OSS
Management
Public cloud site
HQ/DC site
MPLS
site
Branch site
Branch site
CPE
vCPE
IWG
CPE
CPE
MPLS
Internet
Notes: From the perspective of functions, the overall architecture of the SD-WAN Solution consists of the network layer, control layer, and service presentation layer. These layers are associated with each other through standard interfaces and communication protocols.
iMaster NCE-WAN is Huawei's SD-WAN controller, and consists of the service layer (built-in Portal) and control layer.
The enterprise HQ, branches, DCs, and IT infrastructures deployed on the cloud are referred to as enterprise sites.

## Slide 7
Public cloud site
HQ/DC site
MPLS
site
Branch site
Branch site
CPE
Portal for tenants/carriers
RESTful
Southbound NE layer
Northbound network service layer
VPN/Traffic steering/ QoS/Security/WOC
O&M
CPE-VIM
RR
vCPE
Gateway
CPE
No. | Component | Functions
1 | iMaster NCE-WAN | Network service orchestration NE control Basic network O&M CPE orchestration and management Basic performance monitoring (providing link quality information, application quality information, traffic information, as well as statistics from dimensions such as intra-site and inter-site)
2 | RR | Distributes information about inter-CPE VPN routes and tunnels based on VPN topology policies.
3 | CPE | Functions as the egress device of a site, which can be a traditional CPE or Network Functions Virtualization (NFV) vCPE.
4 | Gateway | Connects an SD-WAN network to a non-SD-WAN network.
1
2
3
4
3
CPE
MPLS
Internet
3
Network layer
3
Control layer
Service presentation layer
Key Components of the SD-WAN Solution

## Slide 8: Network Layer Overview
The SD-WAN network of an enterprise consists of two layers: physical network (underlay) and virtual network (overlay), which are completely decoupled from each other.
  Physical network: refers to the underlay WAN provided by a carrier or built by the enterprise itself, including private lines and MPLS networks.
  Virtual network: is also called an overlay network. Huawei SD-WAN Solution introduces IP overlay virtualization technology to construct one or more virtual overlay networks on a physical network. Service policies are deployed on virtual networks and decoupled from the physical network, so that service forwarding is independent of WAN interconnection.
Carrier network/
Enterprise-built network
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
Underlay network
CPE
CPE
CPE
CPE/RR
Notes: Multiple overlay networks can be deployed to provide different services under the same tenant (for example, services of multiple departments) or provide different services for different tenants.
From the perspective of network device functions, the SD-WAN network layer consists of two types of NEs: CPE and gateway.

## Slide 9: CPE Overview
A CPE is an edge node of an SD-WAN network and also called an edge CPE. CPEs are interconnected with each other through IP overlay tunnels.
CPEs are classified into traditional physical CPEs and vCPEs that are deployed at public cloud sites.
All SD-WAN CPEs of an enterprise are centrally managed by iMaster NCE-WAN, and are managed and maintained by tenant administrators.
VPC/vNet
vCPE
CPE
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
CPE
CPE
CPE
CPE/RR
Unified management
IP overlay tunnel
IP overlay tunnel
IP overlay tunnel

## Slide 10: RR Overview
A router reflector (RR) transfers BGP routes and reduces the number of BGP peers.
In Huawei SD-WAN Solution, an RR also controls routes and the network topology. Therefore, an RR is also called an area controller on SD-WAN networks.
Both CPEs at edge sites and RRs are managed by iMaster NCE-WAN.
Control channels are established between RRs and between RRs and edge sites.
RRs are managed by iMaster NCE-WAN, and control route sending and receiving at edge sites based on the overlay network topology model. In this manner, sites can communicate with each other based on the designed overlay topology model.
HQ/DC site
Branch site
Branch site
Management channel
BGP EVPN peer relationship
RR
CPE
(HQ edge)
CPE
(branch edge)
CPE
(branch edge)
MPLS
Internet
Filter overlay routes.
Control the overlay network topology.
Notes: RR site: A CPE functions as an RR and distributes EVPN routes between CPE gateways at edge sites based on the VPN topology policy.
If an egress CPE at a site is configured as both the gateway and RR, this site is an RR site. If no device takes the role of the gateway or RR at a site, the site is an edge site.
One edge site can establish IBGP peer relationships with two RRs simultaneously, and the two RRs back up each other.
Multiple RRs can be deployed for a tenant. All RRs are connected in full-mesh mode on the control plane.

## Slide 11: Gateway Overview
New SD-WAN sites of an enterprise often need to communicate with the enterprise's legacy sites or third-party services. Because some legacy sites are interconnected through MPLS VPN, while SD-WAN sites are interconnected through IP overlay tunnels, SD-WAN sites cannot directly communicate with legacy sites.
An SD-WAN gateway can connect to both SD-WAN and traditional MPLS networks, achieving interconnection between the SD-WAN and traditional MPLS networks.
Traditional MPLS domain
SD-WAN domain
PE
Gateway
PE
MPLS network
SD-WAN
Network
Enterprise 1
Enterprise 2
Enterprise 1
Enterprise 2
Enterprise 3
Notes: A gateway's role name varies depending on the service scenario. For example, a gateway connecting SD-WAN sites to legacy sites is an interworking gateway (IWG), as shown in the above figure. A gateway connecting SD-WAN sites to a cloud is called a cloud gateway. In addition, functions of a gateway can be extended. A gateway that connects Point of Presence (POP) sites for building a POP network is referred to as a POP gateway.

## Slide 12
Architecture and Components of Huawei SD-WAN Solution
Huawei iMaster NCE-WAN
Implementation of Huawei SD-WAN Solution
Huawei SD-WAN CPEs

## Slide 13: Architecture of Huawei iMaster NCE-WAN
Southbound
APIs
Service
functions
Basic
functions
Northbound
APIs
NETCONF
VAS management
Traffic policy
Security policy
Plug-and-play
Visualized O&M
Multi-tenant management
Cluster management
Alarm management
Log management
Device configuration
Tunnel management
Network inspection
Device upgrade
Network devices
CPE
vCPE
Value-added services
(VASs)
OSS/BSS
Analytics system
Other applications
RESTful
SNMP Trap
HTTP/2

## Slide 14: Distributed Cluster Deployment: Supporting Large Scale, High Reliability, and Flexible Capacity Expansion
Huawei iMaster NCE-WAN is deployed using a distributed cluster architecture to provide high reliability and load balancing capabilities. If one cluster node is faulty, other nodes take over services, ensuring service continuity.
Northbound load balancing: External requests are distributed to all cluster nodes, instead of being processed on one node. This makes full use of cluster capabilities and improves reliability.
Southbound load balancing: Cluster nodes are dynamically allocated to network devices based on the load of each cluster node.
Cluster | Functions
Service processing cluster | Provides service processing capabilities, such as CPE management, overlay network configuration delivery, and traffic policy configuration.
Data processing cluster | Provides functions such as CPE performance data storage and data aggregation.
Nginx cluster | Functions as a high-performance HTTP proxy server that forwards concurrent connection requests and performs load balancing for northbound traffic at Layer 4 to Layer 7.
LVS | Functions as a load balancing component that performs load balancing for north-south traffic at Layer 1 to Layer 4.
Distributed clusters of iMaster NCE-WAN
Nginx cluster
Service processing cluster
Data processing cluster
Linux virtual server (LVS)
Physical servers
VMs

## Slide 15: Geographic Redundancy: Fast Switchover Ensures Normal Service Running
Geographic redundancy supports disaster recovery and backup between two clusters. The number of nodes in the active cluster must be the same as that in the standby cluster.
The active and standby controller clusters are both running. However, only the active cluster can provide services, while the standby cluster does not provide services. Data in the active cluster is synchronized to the standby cluster in real time to ensure data consistency.
The northbound and southbound APIs of the controller use the same domain name or IP address. Tenants and devices access the active cluster through the same domain name or IP address. After an active/standby switchover is triggered, traffic is automatically switched to the new active cluster.
Huawei SD-WAN Solution supports only one active controller cluster and one standby controller cluster.
iMaster NCE-WAN cluster (active)
iMaster NCE-WAN cluster (standby)
Branch
site
CPE1
CPE2
CPE3
CPE n
Heartbeat
Data synchronization
Remote DR DC
Primary DC
Administrator
Internet
…
EBGP
(higher priority)
EBGP
(lower priority)
DNS server
Notes: The same IP address or domain name must be configured for the southbound and northbound APIs of the active and standby controller clusters.
Administrators access the controller through the domain name (based on the DNS record) or IP address, and the network uses BGP to control access traffic.

## Slide 16
Architecture and Solutions of Huawei SD-WAN Solution
Huawei iMaster NCE-WAN
Implementation of Huawei SD-WAN Solution
Huawei SD-WAN CPEs

## Slide 17: Main Functions of Huawei SD-WAN Solution
Huawei SD-WAN Solution provides the following functions:
  Zero touch provisioning (ZTP), enabling service provisioning within 1 hour
  Forwarding-control separation, achieving flexible networking
  Application optimization, making services controllable and visible
  Comprehensive security defense system, ensuring service security
Carrier network/
Enterprise-built network
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
Underlay network
CPE
CPE
CPE
CPE
ZTP
IP overlay tunnel 1 (congested)
Application optimization
IP overlay tunnel 2 (smooth)
System hardening
Control channel
Forwarding-control separation
Management channel
RR
Notes: ZTP: Multiple ZTP modes are available to enable CPEs to quickly register with iMaster NCE-WAN.
Forwarding-control separation, achieving flexible networking: CPEs establish management channels with iMaster NCE-WAN through NETCONF, and iMaster NCE-WAN delivers configurations to CPEs to establish IP overlay tunnels.
  Application optimization, making services controllable and visible: Service awareness (SA) technology is used to identify applications. TCP Flow Performance Monitor (FPM) and IP FPM technologies are used to implement application quality detection, and IP FPM technology is used to implement link quality measurement. Smart Policy Routing (SPR) technology implements intelligent link switching based on the application quality.
Comprehensive security defense system, ensuring service security: Multiple VPN technologies, such as IPsec and MPLS, are used to provide E2E security protection. The firewall function provides comprehensive security assurance at the hardware, pipe, and application levels.

## Slide 18: ZTP Overview
With the development of network technologies such as SDN and cloud computing, an increasing number of enterprise networks adopt cloud-based management. However, most sites still need to be deployed by technical engineers onsite, leading to high deployment costs and long deployment period. Huawei offers ZTP to enable quick deployment.
ZTP
Application Optimization
Security
Flexible Networking
ZTP process
Network administrator
Site deployment personnel
CPE
Internet/MPLS
PC
Configure a ZTP configuration file.
1
Transfer the ZTP configuration file.
2
Log in to the PC.
3
Deploy the ZTP configurations.
4
The CPE registers with iMaster NCE-WAN.
5
Notes: ZTP: Zero Touch Provisioning

## Slide 19: ZTP Modes
Huawei SD-WAN Solution supports the following ZTP modes:
Subscription and self-service
Multi-tenant management
MSP/Carrier
Enterprise
Email-based deployment
USB-based deployment
DHCP-based deployment
    Devices are operated in batches in a warehouse and then centrally deployed.
    No high skill requirements are imposed for onsite deployment personnel.
    This mode applies to networks where multiple access modes are used, achieving one-click deployment.
    ZTP configuration files are transferred in different ways depending on the deployment mode.
ZTP
Application Optimization
Security
Flexible Networking
Notes: Files for USB-based, email-based, and DHCP-based deployment can be generated through iMaster NCE-WAN.
For details about each deployment mode, learn the course Management and O&M.

## Slide 20: Flexible Networking
SD-WAN implements flexible and reliable networking of enterprise WANs.
Huawei SD-WAN Solution is implemented based on IP overlay technology, and adopts traditional network technologies such as Layer 2 switching, Layer 3 routing, and VPN isolation. Under the management and control of iMaster NCE-WAN, this solution provides on-demand, flexible, and automatic connections between enterprise branches, DCs, and clouds.
Huawei SD-WAN Solution uses the following types of channels to implement flexible networking:
  Management channel
  Control channel
  Data channel
Management channel:
NETCONF
Control channel:
BGP EVPN
RR
CPE
CPE
Branch site
HQ/DC site
Data channel:
GRE or GRE over IPsec
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE or GRE over IPsec (data channel)
ZTP
Application Optimization
Security
Flexible Networking
Notes: Management channel:
  iMaster NCE-WAN establishes management channels with all managed devices through NETCONF for network-wide device management and service orchestration.
Control channel:
  Control channels are established between CPEs and RRs.
  RRs centrally control and distribute service routes between branch sites.
  The enhanced BGP EVPN protocol is used to implement separate transmission of tenants' VPN routes and next-hop information, and implement IPsec SA negotiation.
Data channel:
  Data channels are established between CPEs.
  Data is forwarded over GRE or GRE over IPsec data tunnels. The extended GRE header carries VN IDs to differentiate tenants or departments, thereby transmitting data of multiple VNs over the same data tunnel.

## Slide 21: Management Channel
Huawei iMaster NCE-WAN establishes management channels with CPEs through NETCONF.
iMaster NCE-WAN delivers configurations through control channels to achieve the following functions:
  Unified management of CPEs, automatic service delivery, and unified control of overlay networks
  Application visualization and automatic application optimization
  Network security services
CPE
NETCONF
(management channel)
NTP configuration
IPsec configuration
Site interconnection configuration
Wireless network configuration
Wired network configuration
IP service configuration
Routing protocol configuration
…
Network administrator
Configure parameters on iMaster NCE-WAN.
Deliver configurations through NETCONF.
1
2
Routing policy configuration
Control layer
Service presentation layer
Network layer
ZTP
Application Optimization
Security
Flexible Networking

## Slide 22: Control Channel
After iMaster NCE-WAN delivers configurations to a CPE through the management channel, the CPE establishes a control channel with an RR through BGP EVPN.
The control channel is used to transmit transport network port (TNP) information, IPsec SA information, and service routes.
After the control channel is established, iMaster NCE-WAN controls route transmission and overlay topology establishment by deploying policies on the RR.
MPLS
Internet
BGP EVPN (control channel)
TNP
IPsec SA
Establish a BGP EVPN peer relationship with the RR based on configurations.
NETCONF
(management channel)
Deliver configurations through NETCONF.
1
2
Transmit TNP, IPsec SA, and service route information through BGP EVPN.
3
Control route transmission based on policies.
4
Service route
Control layer
Network layer
ZTP
Application Optimization
Security
Flexible Networking
Notes: A TNP is a WAN port on a CPE used for connecting to a transport network. The key TNP information includes the site ID, CPE router ID, transport network ID, public IP address, private IP address, and tunnel encapsulation mode.

## Slide 23: Data Channel
Huawei SD-WAN Solution uses GRE or GRE over IPsec to establish data channels.
CPEs establish GRE or GRE over IPsec tunnels based on the TNP and IPsec SA information transferred through BGP EVPN.
CPEs forward data based on the service routes transferred through BGP EVPN.
Service network segment
Service network segment
BGP EVPN
(control channel)
TNP
IPsec SA
MPLS
Internet
Service route
TNP
IPsec SA
Service route
GRE or GRE over IPsec (data channel)
Network layer
ZTP
Application Optimization
Security
Flexible Networking

## Slide 24: Application Optimization
To meet diversified requirements of enterprise applications, traditional WANs have the following issues to resolve:
  Applications of different values are carried on the same link.
  When link quality deteriorates, dynamic routing cannot be implemented.
  No effective measure is available when link quality deteriorates.
To resolve these issues, Huawei SD-WAN Solution offers enterprise experience optimization functions, including:
  Application identification
  Application-based traffic steering
  QoS
  WAN optimization
Application identification
Receiving packets
CPE
Application-based traffic steering
QoS
WAN optimization
Forwarding packets
Application optimization process
ZTP
Application Optimization
Security
Flexible Networking

## Slide 25: Application Identification and Traffic Steering
Huawei SD-WAN Solution uses Smart Application Control (SAC) to identify applications and uses SPR to implement application-based traffic steering.
  SAC enables a device to identify applications and groups application traffic through SA and first-packet identification (FPI).
  SPR enables a device to measure the link quality based on link quality detection packets and determine forwarding paths for traffic.
MPLS
Internet
SPR functional module
Video applications
Internet access services
Voice applications
SAC functional module
Application identification
Application-based traffic steering
1
2
Link quality detection
Link quality detection
Application identification and traffic steering processes
ZTP
Application Optimization
Security
Flexible Networking
Notes: For details about SAC and SPR, learn the course HA Technologies.

## Slide 26: QoS and WAN Optimization
Huawei SD-WAN Solution uses HQoS for bandwidth control and scheduling, and uses Forward Error Correction (FEC) or Adaptive FEC (A-FEC) for WAN traffic optimization.
  HQoS implements hierarchical scheduling based on multi-level queues and differentiates services and users, implementing refined QoS.
  FEC or A-FEC optimization enables the local device to adjust related parameters based on packet loss on the network to generate redundant packets. The peer device then verifies and reassembles the packets.
Application identification and traffic steering
MPLS
Internet
1
2
3
4
Key traffic
HQoS
1
1
2
3
4
Key traffic
Add FEC redundancy packets.
P
Packet loss
1
3
4
Key traffic
P
2
Restore packets through FEC.
2
3
QoS and WAN optimization process
ZTP
Application Optimization
Security
Flexible Networking

## Slide 27: Security Overview
With the emergence of SD-WAN, the traditional closed architecture of enterprise WANs is transformed into an open architecture, which enlarges the attack range and brings new security challenges, including unauthorized access, data leakage, and network attacks.
Huawei SD-WAN Solution provides high security from two perspectives:
  System security: component security and inter-component security
  Service security: firewall, IPS, and URL filtering
RR
CPE
CPE
Branch site
HQ/DC site
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE or GRE over IPsec (data channel)
Management channel security
Control channel security
iMaster NCE-WAN
security hardening
Data channel security
Service traffic security
1
1
1
1
2
CPE security hardening
1
ZTP
Application Optimization
Security
Flexible Networking

## Slide 28: SD-WAN System Security Hardening
SD-WAN system security includes:
  Inter-component security: security of management, control, and forwarding channels
  Component security: security of iMaster NCE-WAN and CPEs
RR
CPE
CPE
Branch site
HQ/DC site
MPLS
Internet
NETCONF over SSH
(management channel)
BGP over IPsec
(control channel)
GRE or GRE over IPsec (data channel)
IPsec ensures the control channel security.
Authentication and authorization ensure the security of iMaster NCE-WAN.
IPsec ensures the data channel security.
Local attack defense, authentication, and other features ensure the CPE security.
SSH ensures the management channel security.
1
1
1
2
2
ZTP
Application Optimization
Security
Flexible Networking

## Slide 29: SD-WAN Service Security
From the perspective of traffic, SD-WAN services are classified into the following types:
  Site-to-site access service
    IPsec ensures security of site-to-site access services.
  Site-to-Internet access service
    The built-in firewall, IPS, and URL filtering functions of CPEs ensure the security of site-to-Internet access services.
  Site-to-cloud access service
    iMaster NCE-WAN is interconnected with a third-party security gateway and controls this gateway to provide security services.
SaaS
GRE or GRE over IPsec
GRE or GRE over IPsec
IPsec ensures security of site-to-site access services.
The firewall, IPS, and URL filtering functions ensure security of site-to-Internet access services.
Interconnect with a third-party security gateway.
CPE
CPE
Internet service server
Third-party security gateway
Control the third-party security gateway to establish an IPsec tunnel with the CPE.
1
2
3
3
ZTP
Application Optimization
Security
Flexible Networking

## Slide 30
Architecture and Solutions of Huawei SD-WAN Solution
Huawei iMaster NCE-WAN
Implementation of Huawei SD-WAN Solution
Huawei SD-WAN CPEs

## Slide 31: Highlights of SD-WAN CPEs
Huawei NetEngine AR series routers function as CPEs and provide extensive SD-WAN features, including hybrid link access, as well as service controllability and visibility. The CPEs reduce WAN interconnection costs and improve O&M efficiency.
5G uplink
Enterprise-class 5G
egress routers
Large bandwidth: 100 Mbit/s UL, 700 Mbit/s DL
Full frequency: 5G, 4G, 3G, and 2G
Dual architectures: standalone (SA) and non-standalone (NSA)
The full lineup of NetEngine AR6000 routers supports 5G.
Ultra-high performance
CPU + NP,
high forwarding performance
Application optimization
Application identification
SEC
HQoS
NP
5 built-in acceleration engines
Optimal experience
Application-based intelligent traffic steering
SD-WAN
Secure
networking
Video
optimization
On-demand VPN interconnection, built-in security functions
Video optimization: A-FEC, ensuring no frame freezing even at 20% packet loss rate
Simplified O&M
ZTP & visualized O&M
Plug-and-play, network provisioning within minutes
Email-, USB-, and DHCP-based deployment
Diversified O&M platforms, real-time intelligent O&M
ZTP & visualized O&M, network provisioning in minutes
On-demand VPN interconnection
Application-based
traffic steering

## Slide 32: Portfolio of Huawei NetEngine AR Routers
NetEngine AR6300
SRU-400H/SRU-600H
NetEngine AR6300/AR6200 series
Small enterprises
AR611W
Ethernet + Wi-Fi
Ethernet + Wi-Fi + LTE
AR611W-LTE4CN
Small/Midsize enterprise branches
HQ/Large branches
NetEngine AR6280
SRU-400H/SRU-600H
NetEngine
AR6100 series
AR6140-16G4XG
AR6121
AR6140-9G-2AC
AR6120
NetEngine
AR650 series
AR651
AR651W
Ethernet + LTE (MIC)
Ethernet + Wi-Fi + LTE (MIC)
SOHO
NetEngine
AR610 series

## Slide 33: Enterprise-Class 5G Branch Routers: Large bandwidth and Low Latency
The full lineup of NetEngine AR6000 series routers supports 5G uplinks.
2G
3G
5G
4G
10x bandwidth
UL
DL
700 Mbit/s
100 Mbit/s
4G core
5G core
5G
4G
5G AR
5G
5G AR
NSA
SA
* Test data
Enterprise-class 5G branch router
Large bandwidth
Full frequency
Dual architectures
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 34: NetEngine AR Routers: Meeting Burst Traffic Requirements of Enterprise Branches
Huawei NetEngine AR series routers are the next-generation routing and gateway devices that provide SD-WAN, routing, switching, VPN, security, voice, and MPLS functions.
5 built-in hardware acceleration engines
Application optimization, application identification, HQoS, SEC, and NP
Ultra-fast algorithm, enabling fast forwarding
Acceleration instruction set, quick ACL and route matching
CPU + NP heterogeneous forwarding
Excellent forwarding performance
NetEngine AR
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 35: 10GE Interconnection and High-Density Access: Building Wide Pipes for Branch Interconnection
NetEngine AR
10GE optical
GE optical/ electrical
5G/LTE
E1/SA...
High-density Ethernet
...
IaaS/SaaS
Internet
HQ/DC
Branch
WAN side
LAN side
10GE uplink, multi-link redundancy, wide pipes for WAN-side interconnection
  High-density 10GE ports: 14 x 10GE optical ports on the SRU-400H and SRU-600H cards; 10GE optical ports on NetEngine AR6000 series routers (except the AR6140-9G-2AC)
  Multi-link redundancy: 10GE, GE optical/electrical, and LTE links
  Flexible switching between LAN and WAN interfaces using commands
High-density access, higher LAN-side access capability
  SRU-400H and SRU-600H: All WAN interfaces can be switched to LAN interfaces.
Flexible card expansion
  Expansion of WSIC, XSIC, SIC, and MIC cards
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 36: Function Convergence: Simplifying Branch Interconnection
Next-generation NetEngine AR routers
On-demand VPN interconnection
Various VPN types
Layer 2 and Layer 3 VPNs
Wi-Fi interconnection of branches
Wi-Fi integration
WAC or Fat AP
Secure interconnection of branches
Built-in security functions
Firewall, IPS, URL filtering, etc.
Wired and wireless convergence
High-density ports, 10GE interconnection, 5G/LTE uplinks
Experience assurance for key applications
Application optimization
A-FEC, application-based intelligent traffic steering (supported only in the SD-WAN Solution)
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 37: Built-in WAC: Reducing Wi-Fi Deployment Costs of Enterprises
eSight
AR (built-in WAC)
RADIUS
server
Enterprise branch network
Enterprise DC
AP
AP
Secure and flexible access
Portal authentication
802.1X authentication
MAC address authentication
Intra-VLAN or inter-VLAN roaming on the same WAC
Application scenarios
Small and midsize enterprises that require wired and wireless convergence
Scenarios where APs use the local forwarding mode and users are centrally authenticated by AR routers
Scenarios where both APs and WACs support Layer 2 and Layer 3 networking
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 38: Wi-Fi Integration for Wired and Wireless Convergence
AR651W
AR611W
/AR611W-LTE4C
Wi-Fi integration for wired and wireless convergence
Wi-Fi functions integrated on fixed AR routers, such as the AR651W, AR611W, and AR611W-LTE4CN
802.11ac/b/g/n, a maximum rate of 1167 Mbit/s
Dual bands (2.4 GHz and 5 GHz), providing stronger wireless user access capabilities
2x2 MIMO
Security: Traditional encryption and authentication ensure terminal access security.
Network management: AR routers function as independent APs to provide functions such as user access, authentication, data security, service forwarding, and QoS.
Networking scale: small-scale networking, requiring low costs
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 39
IPsec
IPsec
HQ
ADSL
5G/LTE
5G/LTE
HQ
  2 major scenarios
  5G/LTE VPN interconnection: wireless access scenarios such as bank ATM interconnection and mobile office
  5G/LTE link backup: enterprise branch interconnection, with wireless links as backup links to ensure service reliability
  5G solution
5G single-chip multi-mode modem
Sub-6G at 200 MHz
  * DL rate: 700 Mbit/s
  * UL rate: 100 Mbit/s
LTE SIC
LTE MIC
AR611W-LTE4CN
  3 types, 4G full frequency
  3 types of LTE modems: LTE SIC (AR6000 series), LTE MIC (AR650 series, except the AR651C), and embedded LTE modem (AR610 series)
  4G full frequency, meeting network standards of different carriers
* Test data
5G/LTE VPN interconnection
5G/LTE link backup
5G/LTE-capable cards and devices
5G SIC
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance
Wireless Uplinks: Leveraging 5G/LTE to Build Wireless Branches

## Slide 40: Comprehensive Security Protection
  Data encryption
  URL filtering
130+ URL categories,
filtering accuracy > 96%
Fine-grained Internet access control
Mainstream VPN encryption protocols
  Application access control
Identification of mainstream encrypted P2P applications
Identification of 6000+ well-known and customized applications
  IPS
IPS engine upgrade
Detection of 5500+ attacks, 90%+ detection rate
  Built-in firewall
State inspection and packet filtering firewall
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 41: Built-in Firewall: Effectively Ensuring Enterprise Network Security
...
Enterprise branch
Malformed packet attack
Application layer attack
DDoS attack
Flood attack
NetEngine AR
(Built-in firewall)
Cloud
Built-in firewall, ensuring branch network security
  Extensive firewall functions
  Packet filtering firewall, quickly matching ACLs and IP addresses to filter network-wide packets
  Application specific packet filter (ASPF), detecting TCP/UDP sessions and filtering out invalid data packets
  Comprehensive attack defense mechanism
  Defense against the following attacks:
  ICMP redirection attacks and ICMP unreachable attacks
  Address scanning and port scanning attacks
  SYN, ICMP, and UDP flood attacks
  Land, Smurf, Fraggle, and WinNuke attacks
  Flexible firewall policies
  Firewall logging, and traffic statistics and monitoring
  Independent security policy deployment for multiple service VPNs through virtual firewalls
  Security policy configuration based on security zones
  Dynamic blacklist for proactive attack defense
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 42: Application Access Control: Extensive Applications, Flexible Upgrade
Signature database (new)
Signature database (old)
Seamless switchover
Protocol 1
Protocol 2
...
New protocol
Protocol 1
Protocol 2
...
Remote signature database file
SA engine
Unclassified packets
Classified packets
Application access control
Signature identification
Correlation identification
Customized application
Application access control
  Identification of 6000+ applications
  Various identification modes: packet signature identification, correlation identification, behavior identification, etc.
  Identification of mainstream protocols (such as P2P, VoIP, IM, game, and email) and 6000+ applications
  Identification of applications customized based on URLs and 5-tuple information
  Flexible upgrade of the SA signature database
  SA signature database files are released and maintained by Huawei Security Competence Center. Customized applications can also be imported.
  Batch or scheduled upgrade of signatures in the SA signature database; periodic release of the new signature database
  Query of the SA signature database upgrade status, including the upgrade time, countdown, progress, and result (success or failure)
  Rollback of the SA signature database upon an upgrade failure
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 43: Comprehensive Access Control and Intrusion Prevention
Denying access to the xx website
Branch
L7 attack packets
Defense against L2–L4 attack packets
L2–L4 attack packets
Normal packets
70%+: L7 attack packets
IPS
Defense against L7 attack packets
  Remote URL category database containing a large number of URLs
  Remote query of 100+ million URLs by category, 130+ predefined categories, category customization, and timely update and efficient query based on Huawei reputation system
  Various URL matching modes
  Prefix matching, suffix matching, keyword matching, exact matching, and quick matching
  Fine-grained blacklist and whitelist
  The blacklist and whitelist are effective supplements to help precisely define and control access to specific websites.
  Flexible response modes
  Various URL filtering actions can be configured to push different URL response pages.
  IPS database with a large number of signatures and a high detection rate
  Attack detection based on 1600+ signatures, with 90%+ detection rate
  Extensive signatures based on network behaviors, such as Trojan horses, worms, botnets, spyware, vulnerability attacks, and web attacks
  Flexible upgrade
  Online upgrade of the signature database and real-time upgrade of the IPS engine, defending against the latest intrusions
  Converged deployment
  The IPS is embedded in AR routers, requiring no dedicated fault detection points while reducing operation costs.
URL filtering
IPS
Firewall
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 44: Application-based Intelligent Traffic Steering: Ensuring Experience of Key Applications
Signature identification
FPI
Customized application
Key applications,
such as video and ERP
MPLS
SLA non-compliance
Internet
Application controllability and visibility
Quick identification of key applications
Application-based intelligent traffic steering, automatically switching traffic of key applications to the optimal link
Intelligent traffic steering based on application SLA, priority, and bandwidth
SLA non-compliance
Automatically switching traffic of key applications to the optimal link
Leveraging hybrid links, such as MPLS, Internet, and LTE
Optimal link selection for traffic of key applications
Customer benefits
Application-based intelligent traffic steering
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 45: A-FEC: Ensuring Smooth Video Experience Even at 20% Packet Loss Rate
WAN
Traditional: frame freezing and artifacts at 2%+ packet loss rate
A-FEC
Real-time detection of application packet loss and adaptive redundancy compensation
Adaptive redundancy compensation
FEC
Link packet loss
Real-time detection of application packet loss
Optimizing experience of video conferencing, live streaming, video surveillance, and VoIP services
NetEngine AR
NetEngine AR
A-FEC: no frame freezing even at 20% packet loss rate
Note: A-FEC is supported only in the SD-WAN Solution.
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 46: ZTP: Achieving Plug-and-Play of Devices in Multiple Scenarios
DHCP
USB flash drive
Email
Network
Power supply
NetEngine AR
Different interfaces: Ethernet, LTE, xDSL...
Different access modes: static IP address, PPPoE, DHCP...
Different scenarios: dual-CPE, batch deployment, device replacement...
Plug-and-play and minute-level device deployment
ZTP for branch network deployment
5G Uplink
Optimal Experience
Simplified O&M
Ultra-High Performance

## Slide 47
(Multiple choices) Which of the following layers are included in the architecture of Huawei SD-WAN Solution?
  Service presentation layer
  Control layer
  Network layer
  Device layer
Notes: 1. ABC

## Slide 48
Architecture and Components of Huawei SD-WAN Solution
  Huawei SD-WAN Solution consists of iMaster NCE-WAN, CPEs, gateways, and RRs.
Huawei iMaster NCE-WAN
  iMaster NCE-WAN has multiple functional modules, and supports geographic redundancy and distributed deployment.
Implementation of Huawei SD-WAN Solution
  Huawei SD-WAN Solution features ZTP, flexible networking, application optimization, and security hardening.
Huawei SD-WAN CPEs
  Huawei SD-WAN CPEs are mainly NetEngine AR series routers.