## Slide 1
V5R2
V1R1
Wu Yue/wwx291773
2020.05.30
New

## Slide 2: SD-WAN Device Deployment

## Slide 3
When building a wide area network (WAN), an enterprise needs to deploy devices at each branch site. However, traditional network deployment modes take an excessively long time for large-scale enterprises.
To accelerate deployment, many vendors have provided functions for deploying devices with zero configurations. However, it is difficult to make deployment files when these functions are used.
The zero touch provisioning (ZTP) function of Huawei SD-WAN Solution greatly shortens the deployment time and simplifies the preparation of deployment files.
This course describes the basic concepts and functions you need to understand during SD-WAN deployment.

## Slide 4
On completion of this course, you will be able to:
  Describe the multi-tenant management boundary of the SD-WAN Solution.
  Describe SD-WAN deployment modes and application scenarios.

## Slide 5
SD-WAN Deployment Overview
Tenant Management
ZTP

## Slide 6: Challenges Facing Traditional Deployment Modes
The provisioning period of traditional private line services is as long as over 30 days, while that of international private line services even reaches 90 days. Traditional branch network deployment also faces the following challenges:
  High technical requirements: Professional IT engineers need to deploy devices on site.
  Low efficiency: Devices are scattered and online operations are time-consuming.
  Misoperation risks: Errors may occur due to manual operations during initial configuration.
Process approval
(2–5 days)
Device installation
(1–3 days)
Device transportation
(2–5 days)
Software commissioning
(1–3 weeks)
Site survey
(1–3 days)
Business consideration & device selection
(1–3 days)
Network planning
(2–5 days)
Branch 1
...
Branch 2
Branch 3
Notes: To address these challenges, the ZTP function of the SD-WAN Solution provides the following benefits:
  Lower technical requirements of site deployment: Device deployment does not require skilled professional IT engineers.
  E2E automatic deployment: The probability of parameter input errors during manual deployment is reduced.
  Centralized planning of offline services for batch devices: Services are provisioned immediately after devices at sites are registered with iMaster NCE-WAN.

## Slide 7: ZTP Modes
ZTP greatly shortens the deployment time. Huawei SD-WAN Solution supports the following ZTP modes:
  Email-based deployment: This mode is commonly and widely used, and has low requirements on site deployment personnel.
  DHCP-based deployment: This mode has almost no requirements for site deployment personnel but requires support from carriers. Therefore, this mode is applicable to only a few scenarios.
  USB-based deployment: This mode has low requirements on site deployment personnel. However, this mode involves many steps and is seldom used on live networks.
Subscription and self-service
Multi-tenant management
MSP/Tenant
Enterprise
Email-based deployment
USB-based deployment
DHCP-based deployment
    Devices are operated in batches in a warehouse and then centrally deployed.
    No high skill requirements are imposed for onsite deployment personnel.
    This mode applies to networks where multiple access modes are used, achieving one-click deployment.
    ZTP files are transferred in different ways depending on the deployment mode.
Notes: DHCP-based deployment and email-based deployment are described in this document.

## Slide 8
SD-WAN Deployment Overview
Tenant Management
ZTP

## Slide 9: Tenant Management Modes
Huawei SD-WAN Solution supports two tenant management modes based on service application scenarios.
  MSP mode: The system administrator creates an MSP, and then the MSP creates tenants.
  Tenant mode: The system administrator creates tenants.
One set of iMaster NCE-WAN manages only one enterprise. Multiple tenants can be created to manage different areas of the enterprise.
This mode applies to enterprise-built SD-WAN interconnection solutions.
Tenant mode
One set of iMaster NCE-WAN can manage multiple enterprises, and different MSP or tenant accounts are allocated to different enterprises. This mode applies to carrier-resold SD-WAN multi-tenant solutions.
MSP mode
Enterprise A
WAN
Enterprise A
WAN
Enterprise B
WAN
Enterprise C
WAN
Notes: Tenant mode: The system administrator creates tenants directly.
  This mode is applicable when an enterprise wants to deploy and manage its own internal network. The system administrator can create multiple tenants to isolate and manage networks of different departments or subsidiaries. Each tenant can create an administrator to manage the tenant's network.
MSP mode: The system administrator creates an MSP, and then the MSP creates tenants.
  This mode is applicable when an enterprise provides network management services for external users. An MSP can be a product distributor, whereas a tenant is a customer who requires network management services.
  The system administrator creates an MSP and specifies an MSP administrator. The specified MSP administrator can create other MSP administrators and specify their management permissions. MSP administrators create tenants and specify tenant administrators. The specified tenant administrators can create other tenant administrators and specify their management permissions.
  A tenant administrator can authorize an MSP to manage the tenant network. In this way, the MSP administrator can maintain the tenant network.

## Slide 10: Multi-Level Service Management
Two multi-level service management modes are available to meet requirements of different business scenarios: "system administrator + MSP + tenant" and "system administrator + tenant".
All tenants share one set of iMaster NCE-WAN, which differentiates tenant data based on tenant identifiers. Data is isolated between tenants, and each tenant possesses independent resources and management permissions.
System administrator
MSP
Tenant
Initial configuration
Operation mode configuration
  MSP operation
Account management
MSP account configuration
Tenant account configuration
Tenant account configuration
Role creation on behalf of tenants
System role configuration
Service configuration
VNF image management
Network configuration on behalf of tenants
Deployment configuration
Network configuration
Traffic policy configuration
Security policy configuration
Site Internet access configuration
Traditional site access configuration
Monitoring and O&M
Network-wide tenant status monitoring
Tenant network inspection
Network monitoring on behalf of tenants
Device monitoring
Site monitoring
Link monitoring
Application monitoring
Fault diagnosis
Cluster monitoring
System monitoring
MSP-managed services are supported.
Notes: Tenants can entrust network O&M services to MSPs so that the MSPs can maintain the tenant networks.

## Slide 11: MSP/Tenant Roles
MSP and tenant roles are defined to specify the access permissions of the MSPs and tenants. The SD-WAN Solution provides the following pre-defined roles:
  Monitor: has the permission to query tenant services and related configurations.
  Open API operator: has the permission to operate open API services and relevant configurations.
  Tenant administrator: has the permission to operate tenant services and relevant configurations.
  Operator: has the permission to manage system service operations.
  CLI operator: has the permission to import device commands by using command line templates.
New roles can be planned based on functions:
  Management role: global administrator, who has all permissions
  Monitoring role: global monitoring personnel who have all monitoring permissions
  Configuration role: network configuration personnel who have the permission to configure the network, traffic policies, and security policies
  O&M role: O&M personnel who have the permission to manage devices, files, and logs

## Slide 12: MSP and Tenant Devices
Devices can be added and deployed under both MSP and tenant accounts. Devices added under an MSP account can only be managed by the MSP, and devices added under a tenant account can only be managed by the tenant.
MSP and tenant accounts are used in different service scenarios. Therefore, the roles of MSP and tenant devices are different.
  Devices added under an MSP account can be used as IWGs or RRs but cannot be used as CPEs.
  Devices added under a tenant account can be used as CPEs or RRs but cannot be used as IWGs.
Public
cloud site
HQ/DC
site
Legacy MPLS site
Branch
site
Branch
site
CPE
RR
CPE
IWG
CPE
CPE
MPLS
Internet
RRs can be added under MSP or tenant accounts.
CPEs can be added only under tenant accounts.
IWGs can be added only under MSP accounts.
Notes: Both MSPs and tenants can deploy devices in ZTP mode.
If a tenant authorizes an MSP to manage its network, the MSP can also manage devices of the tenant.
RRs added under an MSP account are shared RRs, and can be shared by multiple tenants. Shared RRs are used to reduce investment costs.
RRs added under a tenant account are exclusive RRs, and cannot be shared by tenants. Exclusive RRs are used to improve stability.

## Slide 13
SD-WAN Deployment Overview
Tenant Management
ZTP

## Slide 14: Email-based Deployment Overview
During email-based deployment, a network administrator configures deployment information on the iMaster NCE-WAN web UI to generate uniform resource locator (URL) parameters in a deployment email, and then sends the deployment email to a specified deployment mailbox. A deployment engineer receives the deployment email and clicks the URL in the email to start the deployment process. Subsequently, devices are automatically deployed.
Terminals used for deployment
Installation engineer
Network administrator
iMaster NCE-WAN
Egress
1
2
3
4
A network administrator configures and sends a deployment email.
A deployment engineer receives the deployment email.
The deployment engineer performs email-based deployment.
Devices connect to the network and register with iMaster NCE-WAN.
The URL used for deployment can also be sent to the deployment engineer in other ways.
1
2
3
4
Notes: Email-based deployment can be used only in SD-WAN and CloudVPN Solutions.
Email-based deployment applies only to devices with factory settings.
Before email-based deployment of a device, users cannot log in to the web system of the device and change the password. Otherwise, the device will fail to be deployed.
When using the Internet Explorer for email-based deployment, you need to select Use HTTP1.1 on the Internet Options > Advanced tab page of the browser. Otherwise, the device will fail to be deployed.

## Slide 15: Email-based Deployment Details
Before performing email-based deployment, ensure that the following configurations have been completed on iMaster NCE-WAN:
  The email server has been configured.
  Devices have been added.
  Global parameters have been configured.
  Sites have been created.
  The access mode of sites has been configured.
GE0
10.2.1.1/30
AR
MPLS
Internet
GE1
10.2.2.1/30
Underlay network
Network 1
Network 2
Overlay network
CPE 1
Site 1
Send a deployment email.
Send the deployment email.
Deploy the AR based on the email.
The AR goes online.
iMaster NCE-WAN
Email server
Installation engineer
1
2
3
Notes: The email server must be configured by a system administrator or MSP administrator.
  If both the system administrator and MSP administrator have configured an email server, the email server configured by the MSP administrator is used preferentially. If the email server configured by the MSP administrator is unavailable, the email server configured by the system administrator is used.
Devices need to be added to iMaster NCE-WAN in advance.
  Devices can be added under an MSP account or a tenant account.
  Devices added under an MSP account can be used as IWGs or RRs but cannot be used as CPEs.
  Devices added under a tenant account can be used as CPEs or RRs but cannot be used as IWGs.
The global parameter configurations include:
  Physical network configurations: transport network, IPsec encryption, device activation security, link connectivity detection, traffic steering policy parameters, and password of the admin account
  Virtual network configurations: routes, address pools, and DNS
  Collection configurations: network traffic, application quality, and WAN link traffic
To facilitate device management and improve service provisioning efficiency, devices on the same network of a tenant can be added to the same site.

## Slide 16
Notes: The access mode of a site defines information about physical links at the site, such as the interface type, interface IP address, and VPN to which the interface belongs.
  Configuring WAN-side physical links for sites is the prerequisite for site deployment. After a site is configured or activated, WAN-side links can be added or deleted.

## Slide 17: Performing Email-based Deployment
Perform deployment based on the URL in the deployment email. The URL format is as follows:
  https://ip/portal?ac_host=ac_host_value&ac_port=ac_port_value...&url_pass=url_pass_value.
Notes: The URL in a deployment email is in the format of https://ip/portal?ac_host=ac_host_value&ac_port=ac_port_value...&url_pass=url_pass_value.
  Multiple parameters can be configured in the URL and separated by ampersands (&).
  ip indicates the IP address of the web system of the device to be deployed. The default web system IP address and subnet mask of a device are 192.168.1.1 and 255.255.255.0, respectively.

## Slide 18: Checking the Email-based Deployment Result
On the iMaster NCE-WAN web UI, choose Design > Site Agile Design > Devices Management to check whether devices are successfully deployed.
  If the status and administrative status of the devices are normal, the devices are successfully deployed.

## Slide 19: DHCP-based Deployment Overview
DHCP-based deployment is implemented based on the option fields in DHCP packets. The DHCP server is configured with Option 148, which contains address information about iMaster NCE-WAN. Devices obtain such information through DHCP interaction.
The DHCP Option 148 field is usually configured as follows:
  option 148 ascii agilemode=agile-cloud;agilemanage-mode=ip;agilemanage-domain=172.21.16.198;agilemanage-port=10020;
Network administrator
iMaster NCE-WAN
Egress
1
3
4
DHCP server
2
5
A network administrator configures a device's interconnection parameters on iMaster NCE-WAN.
The network administrator configures the DHCP function and sets the Option 148 field.
The device goes online and sends a DHCP Request packet to the DHCP server to apply for an IP address.
The DHCP server replies with a DHCP Response packet carrying the Option 148 field.
The device registers with iMaster NCE-WAN based on the information carried in the Option 148 field.
1
2
3
4
5

## Slide 20: DHCP-based Deployment Details
After the DHCP server is configured, you need to add devices to iMaster NCE-WAN so that the devices can go online.
Sites can be created and the global parameters and site access mode can be configured after devices go online.
After the site access mode is configured on iMaster NCE-WAN, iMaster NCE-WAN sends initial configurations to devices and the devices go online again.
AR
MPLS
Internet
Underlay network
Network 1
Network 2
Overlay network
CPE1
Site 1
Install the AR.
The AR goes online.
iMaster NCE-WAN
Installation engineer
DHCP
server
The AR obtains an IP address.
Send initial configurations.
1
2
3
The AR goes online again.
4
5
Notes: DHCP-based deployment is imperceptible to device deployment personnel, and devices are plug-and-play.

## Slide 21: Checking the DHCP-based Deployment Result
On the iMaster NCE-WAN web UI, choose Design > Site Agile Design > Devices Management to check whether devices are successfully deployed.
  If the status and administrative status of the devices are normal, the devices are successfully deployed.

## Slide 22
(Multiple-choice question) Which of the following roles can be set for the devices added under an MSP account?
  CPE
  RR
  IWG
  Firewall
(True or False) In DHCP-based deployment mode, devices can register with and go online on iMaster NCE-WAN only after the site configuration is complete.
Notes: 1. BC
2. False

## Slide 23
Huawei SD-WAN Solution supports the following user accounts:
  System administrator account, which is used to create MSPs (in MSP mode) or tenants (in tenant mode)
  MSP account, which is used to create tenants and add RRs and IWGs
  Tenant account, which is used to deploy SD-WAN networks
Huawei SD-WAN Solution supports the following ZTP modes:
  Email-based deployment: URL parameters carrying deployment information are sent by email. This mode has low technical requirements on device installation personnel.
  DHCP-based deployment: Devices obtain the IP address of iMaster NCE-WAN through DHCP. This mode has almost no technical requirements on device installation personnel.
  USB-based deployment: USB flash drives are used to transmit deployment information. This mode has low technical requirements on device installation personnel.