## Slide 1
SD-WAN
V1R19C00
Hou Jianqiang/0405872
2019-12-16
Wu Yue/wwx291773
2020-10-5

## Slide 2: SD-WAN Networking and Planning

## Slide 3
To meet service development requirements, enterprises require flexible and reliable wide area networks (WANs).
Huawei offers an SD-WAN networking sub-solution to help enterprises implement on-demand, flexible, automated networking between enterprise branches, data centers (DCs), and clouds through the SD-WAN controller (iMaster NCE-WAN).
This course describes the implementation and design of SD-WAN flexible networking.

## Slide 4
Upon completion of this course, you will be able to:
  Describe basic implementations of SD-WAN flexible networking.
  Describe the networking schemes of the SD-WAN Solution.
  Complete the planning and design of an enterprise SD-WAN network using the design principles and methods described in this course.

## Slide 5
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
SD-WAN Networking Design

## Slide 6: Flexible Networking of Huawei SD-WAN Solution
Huawei SD-WAN Solution uses iMaster NCE-WAN to centrally manage devices and flexibly establish IP overlay tunnels, through which service traffic is forwarded.
Huawei SD-WAN Solution implements flexible networking through the following channels:
  Management channel: connects iMaster NCE-WAN to the control layer, so that iMaster NCE-WAN provides service portal pages for SD-WAN service presentation and configuration delivery.
  Control channel: controls establishment of IP overlay tunnels and transmits service routes.
  Data channel: forwards data over carrier networks or enterprise-built networks and allows for flexible traffic steering based on network Service Level Agreement (SLAs).
Management channel:
NETCONF
Control channel:
BGP EVPN
RR
CPE
CPE
Branch
site
HQ/DC site
Data channel:
GRE or GRE over IPsec
MPLS
Internet
NETCONF
(management channel)
BGP EVPN
(control channel)
GRE or GRE over IPsec (data channel)
Notes: In Huawei SD-WAN Solution, IP overlay tunnels are mainly GRE or GRE over IPsec tunnels.
Services on the management plane are mainly implemented by iMaster NCE-WAN.
This course mainly describes the implementation principles of services on the control plane and forwarding plane.

## Slide 7: Components of Huawei SD-WAN Solution
iMaster NCE-WAN: controls network elements (NEs) on the entire SD-WAN network, orchestrates network services, and performs monitoring and O&M.
Route reflector (RR): also called an area controller, distributes VPN routing and tunnel information between CPEs based on VPN topology policies.
CPE: refers to an AR router deployed at the egress of a campus network.
Edge site: A CPE is used as the edge router on the WAN side. A control channel is established between the edge site and RR. The RR controls route advertisement. Secure data channels are established between multiple sites. A CPE at the edge site is the source or destination of an EVPN interconnection tunnel, and can be considered as the border of an EVPN network.
HQ/
DC site
Branch site
Branch site
Management channel
Control channel: BGP EVPN peer relationship
RR
CPE
(HQ edge)
CPE
(branch edge)
CPE
(branch edge)
MPLS
Internet

## Slide 8: Management Channel
iMaster NCE-WAN establishes management channels with CPEs through NETCONF.
Management channels are used for:
  Unified management of CPEs, automatic service delivery, and unified control of overlay networks
  Network status monitoring and automatic application optimization
  Device status monitoring
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
CPE
CPE
Data channel
Data channel
Data channel
CPE/RR
CPE
NETCONF
(management channel)

## Slide 9: Control Channel
Control channels are established between CPEs and RRs through BGP EVPN to control the establishment of data channels and transmission of service routes.
  An RR reflects transport network port (TNP) information, IPsec SA information, and service routes. Typically, an RR is deployed at an HQ site.
  IP overlay tunnels (data channels) are established mainly depending on TNP and IPsec SA information.
  When service routes are reflected by an RR, the RR can control transmission of the service routes based on routing policies (typically delivered by iMaster NCE-WAN) to control the service traffic direction.
  An RR is also called an area controller.
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
CPE
CPE
CPE
CPE
Data channel
Data channel
Data channel
RR
BGP
(control channel)
An RR is typically deployed at the HQ site.
Notes: TNP information and other related information will be described in the following slides.

## Slide 10: Data Channel
Data channels are established between CPEs through GRE or GRE over IPsec. A network built by data channels is called an overlay network, which is constructed on an underlay network.
  An overlay network is constructed based on data channels. Different overlay networks can be constructed for different services or departments.
  An underlay network is a traditional WAN-side network and mainly carries services of overlay networks. An underlay network can be the Internet, an MPLS network, or an enterprise-built network.
Carrier network/
Enterprise-built network
Branch site
Branch site
Enterprise HQ
Branch site
Overlay network
Underlay network
CPE
CPE
CPE
CPE/RR
Data channel
Data channel
Data channel

## Slide 11: Basic Concepts of Huawei SD-WAN Networking
Transport network (TN): refers to a WAN access network provided by an ISP, which implements WAN interconnection of enterprise branches.
Routing domain (RD): If different TNs can communicate with each other (for example, the Internet networks provided by ISPB and ISPC in the figure on the right), they are considered to be in the same RD.
Site ID: indicates the globally unique ID of a tenant site, which is allocated by iMaster NCE-WAN.
CPE router ID: indicates the globally unique ID of a CPE. A site can have one or two CPEs. The router ID of a CPE is typically the CPE's loopback interface address.
  WAN link: refers to a link connecting to a WAN interface. The IP address allocation mode, link negotiation rate, and bandwidth can be configured for a WAN link.
TNP: refers to the WAN interface on a CPE for connecting to a transport network. The key information about a TNP includes the site ID, CPE router ID, transport network ID, public IP address, private IP address, and tunnel encapsulation mode.
HQ site
RD: Internet
RD: MPLS
Branch site 1
Site ID: AAA
Site ID: BBB
CPE1
CPE2
Site ID: CCC
Branch site 2
3.3.3.3
(CPE router ID)
4.4.4.4
(CPE router ID)
5.5.5.5
(CPE router ID)
1.1.1.1
(CPE router ID)
2.2.2.2
(CPE router ID)
GE0
GE1
GE0
GE1
GE0
GE1
GE0
CPE3
CPE4
MPLS-ISPA
(TN)
Internet-ISPB (TN)
Internet-ISPC (TN)
CPE5
WAN link
WAN link
TNP
Notes: TN and RD information are used for enumerating and establishing overlay tunnels.
A site ID is used as the next hop for addressing and data forwarding during user routing.
CPEs' router IDs are defined for establishing BGP peer relationships between sites.
TNPs are defined for establishing tunnels.

## Slide 12: TNP
A TNP mainly describes WAN link information about a site, depending on which control and data channels are established.
The following table describes TNP information.
TNP Information | Example |  | Description
Site ID | 111 |  | Site to which the TNP belongs
CPE Router ID | 1.1.1.1 |  | CPE to which the TNP belongs
TNP ID | 1 | 2 | TNP number
Transport Network | TN1 | TN2 | TN to which the TNP belongs
Routing Domain | RD1 | RD1 | RD to which the TNP belongs
Public IP | 10.2.1.1 | 202.2.2.1 | WAN-side public IP address (post-NAT)
Private IP | 10.2.1.1 | 10.2.2.1 | WAN-side private IP address (pre-NAT)
Encapsulation | GRE | GRE | Encapsulation mode
Site ID: 111
1.1.1.1
(CPE router ID)
GE0
10.2.1.1/30
CPE1
MPLS-ISPA
(TN1)
Internet-ISPB (TN2)
GE0
202.2.2.1/30
GE1
10.2.2.1/30
NAT device of ISPB
RD: RD1
Notes: TN and RD information are used for enumerating overlay tunnels.
  Tunnel enumeration ensures that all available tunnels are established.
A router ID is used for establishing a control channel.
A site ID specifies the next hop for data forwarding.
An interface number can be used as a TNP ID.
The public and private IP addresses refer to the source and destination IP addresses of the control and data channels.
  To establish a data channel between CPEs behind NAT devices, the CPEs need to learn the post-NAT IP addresses (public IP addresses).
    Typically, a CPE learns public IP addresses through STUN technology.

## Slide 13: RD and TN
A CPE enumerates data tunnels based on the RD and TN IDs in the TNP information.
Tunnel enumeration ensures the reliability of SD-WAN networks and improves service awareness.
Tunnel enumeration rules:
  Only TNPs in the same RD can be connected with each other in enumeration mode and fully meshed.
  TNPs in different RDs cannot be connected in enumeration mode.
RD: Internet
RD: MPLS
CPE1
CPE2
GE0
GE1
GE0
GE1
GE0
CPE3
MPLS-ISPA
(TN)
Internet-ISPB (TN)
Internet-ISPC (TN)
TNPs in the same RD are connected to each other in full-mesh mode.
Notes: Tunnel enumeration is performed before data channel establishment to ensure that all available data channels are established.
Prerequisites for tunnel enumeration:
  CPEs have learned service routes from the peer site.
  CPEs have learned TNP information from the peer site.
The details about how to learn service routes and TNP information will be described in the following slides.

## Slide 14
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
  Implementation of Flexible Networking
  Flexible Networking Features
SD-WAN Networking Design

## Slide 15: SD-WAN Networking Process
The SD-WAN networking process is as follows:
Management channel establishment
A network administrator configures WAN link parameters for CPEs and RRs on iMaster NCE-WAN.
An installation engineer delivers the WAN link parameter configurations to the CPEs and RRs through ZTP.
The CPEs and RRs proactively register and establish NETCONF channels (management channels) with iMaster NCE-WAN.
Control channel establishment
After iMaster NCE-WAN delivers configurations to the CPEs and RRs through the management channels, the CPEs establish DTLS management channels with the RRs.
The CPEs exchange TNP and IPsec SA information with the RRs.
The CPEs establish BGP EVPN control channels with the RRs based on the TNP and SA information.
Data channel establishment and data forwarding
The RRs reflect the TNP and IPsec SA information about the CPEs.
The RRs reflect service routes of the CPEs.
After the TNP and IPsec SA information is advertised, the CPEs are triggered by routes to establish data channels with each other.
Network administrator
1
2
3
Installation engineer
NETCONF
(management channel)
CPE/RR
CPE
CPE
Data channel
TNP
IPsec SA
Service route
TNP
IPsec SA
Service route
3
1
2
DTLS management channel
DTLS management channel
BGP control channel
BGP control channel
CPE
CPE
RR
2
1
3
TNP
IPsec SA
Notes: A management channel is used for establishing control channels and delivering basic configurations.
Control channels are used to control establishment of data channels.
Data channels transmit user data.
TNP information is exchanged twice as follows:
  TNP information is exchanged for the first time for establishing control channels between RRs and CPEs.
  TNP information is exchanged for the second time for establishing data channels between CPEs.

## Slide 16: Management Channel Establishment
Once a CPE registers with iMaster NCE-WAN through ZTP, a management channel is established between them.
Through the management channel, iMaster NCE-WAN delivers the following information to the CPE: TNP information (including the site ID, CPE router ID, device role, RD ID, and TN ID), interface configurations and IP addresses, as well as basic BGP configurations.
The information transmitted through the management channel is mainly used for controlling data channel establishment.
RR
CPE
HQ edge
CPE
Branch edge
MPLS
/Internet
Site ID: 222
Router ID: 2.2.2.2
Public/Private IP2, RD1, TN1
Loopback 1: 1.1.1.1/32
Tunnel 1: 10.1.1.1/32
BGP Peer 3.3.3.3
Site ID: 111
Router ID: 1.1.1.1
Public/Private IP1, RD1, TN1
Loopback 2: 2.2.2.2/32
Tunnel 2: 10.2.2.2/32
BGP Peer 3.3.3.3
Loopback 3: 3.3.3.3/32
Tunnel3: 10.3.3.3/32
BGP Peer 1.1.1.1
BGP Peer 2.2.2.2
Address pool
RRs to which CPEs belong
…
Service presentation layer
iMaster NCE-WAN delivers TNP information to CPEs.
Basic BGP configurations
The IP addresses of loopback and tunnel interfaces are allocated from the address pool.
iMaster NCE-WAN delivers interface configurations and basic BGP configurations to CPEs.
NETCONF over SSH (management channel)
Site ID: 333
Router ID: 3.3.3.3
Public/Private IP3, RD1, TN1
Management Channel
Data Channel
Control Channel
Data Forwarding
Notes: For details about ZTP and management channel establishment, learn the course SD-WAN Deployment.
An RR is typically deployed at the same site as CPEs of the HQ. For ease of understanding, an RR is deployed independently of CPEs of the HQ in the above figure.
All configurations on the CPEs and RR are delivered by iMaster NCE-WAN.
The IP address of a CPE's loopback interface is used as the CPE's router ID.
Tunnel interfaces are used for establishing management channels, which use the GRE over IPsec encapsulation mode.
iMaster NCE-WAN also delivers basic BGP configurations to instruct CPEs to establish BGP peer relationships with the RR through loopback interfaces.
Site IDs are generally allocated to CPEs in ascending order based on the sequence in which the CPEs go online.

## Slide 17: Control Channel Establishment
Control channels use BGP to transmit data channel parameters. To ensure the control channel security, BGP is carried over EVPN tunnels.
Control channels mainly transmit TNP information, IPsec SA information, and service routes. The TNP and IPsec SA information is used for establishing data channels. Service routes are used for traffic steering during data forwarding.
RR
CPE
HQ edge
CPE
Branch edge
MPLS
/Internet
DTLS channel
1
Site ID: 222
Router ID: 2.2.2.2
Public/Private IP2, RD1, TN1
Loopback 1: 1.1.1.1/32
Tunnel 1: 10.1.1.1/32
BGP Peer 3.3.3.3
Site ID: 111
Router ID: 1.1.1.1
Public/Private IP1, RD1, TN1
Loopback 2: 2.2.2.2/32
Tunnel 2: 10.2.2.2/32
BGP Peer 3.3.3.3
Site ID: 333
Router ID: 3.3.3.3
Public/Private IP3, RD1, TN1
Loopback 3: 3.3.3.3/32
Tunnel3: 10.3.3.3/32
BGP Peer 1.1.1.1
BGP Peer 2.2.2.2
EVPN tunnel
2
EVPN tunnel
BGP control channel
3
Management Channel
Data Channel
Control Channel
Data Forwarding
Notes: A control channel is established as follows:
  A CPE establishes a DTLS tunnel with an RR based on the TNP information delivered by iMaster NCE-WAN.
    The DTLS tunnel is established to ensure security of TNP information exchanged between the CPE and RR.
  The CPE and RR exchange TNP and IPsec SA information through the DTLS tunnel, and establish an EVPN tunnel based on the TNP and IPsec SA information.
    In Huawei SD-WAN Solution, EVPN tunnels use the GRE over IPsec encapsulation mode.
    The source and destination IP addresses of an EVPN tunnel are determined by the TNP information about the CPE and RR.
  The CPE and RR establish a BGP peer relationship through loopback interfaces.
    All CPEs are BGP RR clients of the RR.
    The CPE and RR send BGP packets to each other to exchange the TNP and IPsec SA information required for establishing data channels.

## Slide 18: TNP and IPsec SA Information Exchange
An RR can reflect TNP and IPsec SA information about different CPEs through control channels.
After TNP and IPsec SA information is exchanged, CPEs cannot establish data channels immediately with each other. Instead, data channel establishment between them is triggered by service routes.
RR
CPE
HQ edge
CPE
Edge of branch 1
MPLS
/Internet
Site ID: 222
Router ID: 2.2.2.2
Public/Private IP2, RD1, TN1
IPsec SA2
Site ID: 111
Router ID: 1.1.1.1
Public/Private IP1, RD1, TN1
IPsec SA1
Exchange TNP and IPsec SA information through control channels.
Reflect the TNP and IPsec SA information sent from CPEs.
BGP control channel
1
2
CPE
Edge of Branch 2
Site ID: 444
Router ID: 4.4.4.4
Public/Private IP4, RD1, TN1
IPsec SA4
BGP control channel
BGP control channel
TNP | IPsec SA
TNP of the HQ | IPsec SA of the HQ
TNP of Branch 1 | IPsec SA of Branch 1
TNP of Branch 2 | IPsec SA of Branch 2
TNP | IPsec SA
TNP of the HQ | IPsec SA of the HQ
TNP of Branch 1 | IPsec SA of Branch 1
TNP of Branch 2 | IPsec SA of Branch 2
TNP | IPsec SA
TNP of the HQ | IPsec SA of the HQ
TNP of Branch 1 | IPsec SA of Branch 1
TNP of Branch 2 | IPsec SA of Branch 2
Management Channel
Data Channel
Control Channel
Data Forwarding
Notes: TNP and IPsec SA information is exchanged as follows:
  Through the BGP control channel, a CPE sends the local TNP and IPsec SA information to the RR through a BGP route.
    The RD ID and TN ID in the TNP information are used for enumerating and establishing data tunnels.
    The public and private IP addresses are used as the source and destination IP addresses of a data tunnel.
    IPsec SA information is used to encrypt the data tunnel.
    The site ID is used for traffic steering. The functions of a site ID will be detailed in the following slides.
  The RR sends the BGP route received from the CPE to all CPEs associated with the RR.

## Slide 19: Service Route Transmission and Data Channel Establishment
MPLS
/Internet
CPEs' service routes are transmitted through BGP control channels.
Based on the next hop of a service route as well as the TNP and IPsec SA information, a CPE is triggered to create a data channel with the peer CPE.
  The next hop of an SD-WAN service route is determined by the site ID.
  The CPE searches the connection table for TNP information based on the site ID, and then enumerates data channels based on the TNP information.
HQ
Site ID: 111
Branch
Site ID: 222
RR
Service 1
Reflect service routes.
BGP control channel
2
Service 1
VRF1 routing table
Prefix NextHop
10.0.0.0/24 Local
10.1.0.0/24 222
BGP control channel
Service 1
VRF1 routing table
Prefix NextHop
10.0.0.0/24 111
10.1.0.0/24 Local
1
Establish data channels based on service routes.
3
Service 2
GRE over IPsec tunnel (MPLS)
1
Service 2
VRF2 routing table
Prefix NextHop
20.0.0.0/24 Local
20.2.0.0/24 222
1
Service 2
VRF2 routing table
Prefix NextHop
20.0.0.0/24 111
20.2.0.0/24 Local
1
Management Channel
Data Channel
Control Channel
Data Forwarding
Notes: Data channels use the GRE over IPsec encapsulation mode.
VPN technology is used to isolate routes of different services.
  Different service routes belong to different VPNs. Therefore, different service routes are placed in different VRF routing tables.
Multiple links may be established between different CPEs. If different routes of a service are in the same RD, the CPEs enumerate data channels.
  Each data channel is also called an EVPN connection.
  Multiple data channels are carried in one GRE over IPsec tunnel.

## Slide 20: Service Data Forwarding Process
After a data channel is established between CPEs, the CPEs will select data channels based on the routing and connection tables for data forwarding.
HQ
Site ID: 111
Branch
Site ID: 222
Net: 10.1.0.0/24
Service 1
VRF routing table
Prefix NextHop
10.0.0.0/24 Local
10.1.0.0/24 222
Connection table
Connection-ID Site-ID Src-TNP Des-TNP
1 222 TNP1 TNP2
2 222 TNP3 TNP4
Des IP: 10.1.0.0/24 | Data
IP | ESP | ExtGRE | Data
Search the routing table for a service route based the destination IP address of the data packet.
1
Search the connection table for the next-hop site ID of the service route.
2
Select a data channel from the connection table and encapsulate the data packet based on TNP information.
3
Send the data packet to the peer CPE.
4
Add the VPN field to the ExtGRE header of the data packet.
Management Channel
Data Channel
Control Channel
Data Forwarding
MPLS
/Internet
GRE Over Ipsec Tunnel1
GRE Over Ipsec Tunnel2
Notes: There may be multiple data channels destined for the same site ID. Therefore, a CPE needs to select a data channel for data forwarding.
  Typically, a data channel is selected based on the priority. However, there are various data channel selection policies. For details, learn the course SD-WAN Application Experience.
Data transmitted over a data tunnel will be re-encapsulated before being sent.
  The data encapsulation mode is GRE over IPsec.
  The VPN field is added to the ExtGRE header to identify the service (VPN) to which the data belongs during data forwarding.

## Slide 21: Service Traffic Isolation
In Huawei SD-WAN Solution, routes of different services are placed in different VRF routing tables for isolation.
On the forwarding plane, the VPN field in the ExtGRE header is used to differentiate service traffic.
HQ
Site ID: 111
Branch
Site ID: 222
Service 1
Service 2
GRE over IPsec tunnel
IP | ESP | ExtGRE | Data
IP | ESP | ExtGRE | Data
VPN1
VPN2
Management Channel
Data Channel
Control Channel
Data Forwarding

## Slide 22
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
  Implementation of Flexible Networking
  Flexible Networking Features
SD-WAN Networking Design

## Slide 23: Challenges Facing Flexible Networking
SD-WAN flexible networking faces the following challenges on the live network:
  How to flexibly control the overlay topology?
  How to establish data channels between CPEs behind NAT devices?
MPLS/Internet
Diversified overlay topology requirements
Different services may use different overlay topologies.
In addition to hub-spoke networking and full-mesh networking, partial-mesh networking may be used.
Establishment of data channels between CPEs through NAT traversal
On the live network, some CPEs are deployed behind NAT devices.
The CPEs behind NAT devices cannot directly establish data channels with each other.
Site1
Site2
Site3
Site4
HQ/DC
MPLS/Internet
HQ
CPE
Branch
CPE
Data channel
NAT device
NAT device

## Slide 24: Overlay Topology Control
Branch
Site ID: 444
Data channels of CPEs constitute an overlay topology and are established mainly depending on service routes.
  CPEs establish data channels based on the next-hop site ID of service routes and TNP information.
  Establishment of a data channel can be controlled by controlling the next-hop site ID of a service route.
  When establishment of data channels is controlled, the overlay topology is controlled.
Overlay Topology
NAT Traversal
MPLS
/Internet
HQ
Site ID: 111
Branch
Site ID: 222
RR
Change the next-hop site ID of service routes when reflecting the service routes.
BGP control channel
BGP control channel
VRF routing table
Prefix NextHop
10.0.0.0/24 111
10.1.0.0/24 111
10.2.0.0/24 Local
VRF routing table
Prefix NextHop
10.0.0.0/24 Local
10.1.0.0/24 222
10.2.0.0/24 444
VRF routing table
Prefix NextHop
10.0.0.0/24 111
10.1.0.0/24 Local
10.2.0.0/24 111
Data channel
Data channel
Notes: Different services may use different overlay topologies.
Because an RR reflects service routes of all CPEs associated with it, the RR can change the next-hop site ID of service routes to control the overlay topology.
When the hub-spoke topology is used, the RR only needs to change the next-hop site ID of service routes to the site ID of the hub site.
When the full-mesh topology is used, a full-mesh network can be built without the need to change the next-hop site ID of service routes.
When the partial-mesh topology is used, the next-hop site ID of only some service routes needs to be changed.
Because an RR can control the overlay topology, it is also called an area controller.

## Slide 25: NAT Traversal
Private
network
Although NAT allows private network users to access a public network, it has the following defects:
  Private IP addresses are hidden, making it difficult for external network devices to access private network devices.
To allow CPEs deployed behind NAT devices to directly establish data channels with each other, Huawei SD-WAN Solution adopts Session Traversal Utilities for NAT (STUN) technology.
Private
network
NAT traversal
MPLS/Internet
NAT device
NAT device
Overlay Topology
NAT Traversal

## Slide 26: Overview of STUN
By leveraging the cone NAT feature, NAT traversal technology is used to create NAT mapping entries on NAT devices and then perform hole punching on the NAT devices. In this manner, connections can be established between private networks based on the NAT mapping entries.
STUN is mainly used to obtain hole punching information (namely, the mapping between pre-NAT private IP addresses and port numbers and post-NAT public IP addresses and port numbers) on NAT devices. CPEs establish data channels traversing NAT devices using other technologies.
NAT traversal
Private network
Private
network
Internet
NAT device
NAT device
IP1
Port1
IP2
Port2
IP3
Port3
IP4
Port4
NAT mapping table
NAT mapping table
Private IP Address: Port Number | Public IP Address: Port Number
IP1:Port1 | IP2:Port2
Private IP Address: Port Number | Public IP Address: Port Number
IP4:Port4 | IP3:Port3
Overlay Topology
NAT Traversal
Notes: STUN is defined in RFC 3489 and is a complete NAT traversal solution.
In RFC 5389, the STUN protocol is positioned as a tool used to allow packets to traverse NAT devices, rather than a complete solution. RFC 5389 supports TCP traversal, which is not supported in RFC 3489.

## Slide 27: STUN Fundamentals
STUN is implemented as a client-server protocol. Through packet exchange with a STUN server, a STUN client can detect a NAT device and determine the IP address and port number allocated by the NAT device.
STUN fundamentals
Private
network
Internet
NAT mapping table
IP1
Port1
Private IP Address: Port Number | Public IP Address: Port Number
IP1:Port1 | IP2:Port2
STUN server
STUN client
NAT translation
SIP: IP1
STUN binding request
S Port: Port1
SIP: IP2
STUN binding request
S Port: Port2
Obtain the source IP address and port number from the STUN binding request and add them to a STUN binding response.
DIP: IP2
STUN binding response
D Port: Port2
NAT translation
DIP: IP1
STUN binding response
D Port: Port1
Record the mapping between the private IP address + port number and the public IP address + port number.
IP=IP2, Port=Port2
NAT device
IP2
Port2
IP1:Port1 <-> IP2:Port2
Overlay Topology
NAT Traversal

## Slide 28: Data Channel Establishment Traversing NAT Devices
In SD-WAN scenarios, STUN can be used to allow CPEs deployed behind NAT devices to establish data channels traversing NAT devices.
Data channel establishment traversing NAT devices
Private IP Address: Port Number | Public IP Address: Port Number
IP1:Port1 | IP2:Port2
Private
network
Private
network
Internet
NAT device
NAT device
IP1
Port1
IP2
Port2
IP3
Port3
IP4
Port4
RR (STUN server)
CPE
(STUN client)
CPE
(STUN client)
STUN binding request
STUN binding request
STUN binding response
STUN binding response
Private IP Address: Port Number | Public IP Address: Port Number
IP4:Port4 | IP3:Port3
Learn TNP and route information
from the peer end through BGP.
1
1
2
2
3
Establish a data channel
traversing the NAT devices.
4
Overlay Topology
NAT Traversal
Notes: Each STUN client sends a binding request to the STUN server.
The STUN server obtains the source IP address and port number from the binding request, and sends a binding response to each STUN client.
The STUN client obtains an IP address and a port number from the binding response, and compares the obtained IP address and port number with the source IP address and port number carried in the binding request. If they are different, a NAT device is used between the STUN client and STUN server.
STUN clients learn each other's TNP information (including the pre-NAT and post-NAT IP addresses and port numbers) through BGP routes.
After the preceding STUN messages are exchanged, a data channel is established between the STUN clients traversing the NAT devices based on the hole punching mechanism.

## Slide 29
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
SD-WAN Networking Design
  Site Design
  Overlay Network Design
  Network Service Design

## Slide 30: Typical WAN-side Networking Modes of Sites
Single-site single-CPE networking (a single CPE supporting a maximum of 3 links)
Enterprise intranet
Enterprise intranet
Enterprise intranet
MPLS
/Internet
MPLS
Internet
MPLS
Internet
LTE
MPLS
INET
LTE
MPLS
INET
MPLS
INET
MPLS
INET
Enterprise intranet
Enterprise intranet
Enterprise intranet
Enterprise intranet
Single-site dual-CPE networking (a maximum of 6 links, with each CPE supporting a maximum of 3 links)
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 31: Underlay WAN-side Routing: BGP and OSPF
When a CPE is connected to an MPLS WAN network and the PE uses OSPF to exchange routes, OSPF needs to be deployed on the CPE.
iMaster NCE-WAN can configure OSPF priorities and configure blacklist- or whitelist-based route filtering policies to control the advertisement and receiving of OSPF routes.
If a CPE is connected to an MPLS WAN network and the PE uses BGP to exchange routes, the CPE typically needs to use BGP to exchange routing information with the PE.
iMaster NCE-WAN can configure route filtering rules based on IP network segments to control the advertisement and receiving of BGP routes.
CPE (CE)
PE
BGP
CPE (CE)
PE
OSPF
MPLS
MPLS
WAN connection using BGP
WAN connection using OSPF
WAN-side Networking
LAN-side Networking
Dual-Gateway
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 32: Underlay WAN-side Routing: Static
LTE
Static routes are used in many scenarios. For example, default static routes are configured for Internet access, and blackhole routes are configured to prevent loops.
On the live network, static routes do not involve protocol interaction and cannot detect faults on indirectly connected links of the WAN. This may cause service interruption.
When configuring a static route on a CPE, you can enable the track function and use an NQA test instance to detect the link quality. If the detection fails, the CPE considers that the WAN is faulty and automatically selects the backup link for data forwarding, preventing long-time service interruption.
CPE
12.1.1.1
200.1.1.1
NQA Test
mytest1
[CPE] ip route-static 10.1.0.0 16 12.1.1.1 track nqa admin mytest1
[CPE] ip route-static 10.1.0.0 16 200.1.1.1 preference 80
MPLS
Internet
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 33: Typical LAN-side Networking Modes of Sites
Interconnection with a Layer 2 network or hosts on the LAN side (through a CPE that functions as a gateway)
Interconnection with a Layer 3 network on the LAN side through BGP, OSPF, or static routes
Layer 2 switch
VRRP
VRRP
Direct connection
BGP
OSPF
Direct
Static
Layer 3 switch
BGP
OSPF
Direct
Static
BGP
OSPF
Direct
Static
BGP
OSPF
Direct
Static
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 34: LAN-side Site Model: Layer 2 Interconnection
AR (CPE)
Layer 2 switch
AR (CPE)
VRRP
AR (CPE)
AP
AR (CPE)
Layer 2 switch
Single-CPE Layer 2 interconnection
Dual-CPE Layer 2 interconnection
If a site has only one CPE and a small scale, the CPE can be directly connected to terminals at the site through LAN-side interfaces.
If the CPE has insufficient LAN-side interfaces, an access switch can be connected to the CPE.
When a site has two CPEs, VRRP is usually deployed on the CPEs.
LAN-side switches can be stacked.
An interlink needs to be established between the CPEs to forward service packets between them.
WAN-side Networking
LAN-side Networking
Dual-Gateway
Notes: If a site has only one CPE, LAN-side connections are simple.
  If the site has a small scale (for example, a SOHO site), the CPE can be directly connected to terminals at the site through LAN-side interfaces.
  If the CPE has insufficient LAN-side interfaces, an access switch can be connected to the CPE through one-armed routing.
If a site has two CPEs, VRRP is deployed on the CPEs to prevent the dual-CPE architecture from affecting the LAN-side network.
  Multiple switches can be deployed on the LAN side to form a stack. If two CPEs are deployed at a site, they can be interconnected directly or through the LAN-side network.
  If the two CPEs are directly interconnected, an interlink needs to be established between them to forward service packets. The interlink can also be an Eth-Trunk.

## Slide 35: LAN-side Site Model: Layer 3 Interconnection
In the Layer 3 interconnection scenario, if only one CPE is deployed at a site, only a routing protocol needs to be configured on the LAN side based on requirements of LAN-side devices.
In the Layer 3 interconnection scenario, a CPE can only interconnect with a standalone device or a stack on the LAN side. Therefore, when a CPE needs to interconnect with multiple devices, these devices must be stacked.
AR
Layer 3 switch
AR
Layer 3 switch
AR
Static
OSPF
BGP
Static
OSPF
BGP
Single- or dual-CPE Layer 3 interconnection
WAN-side Networking
LAN-side Networking
Dual-Gateway
Notes: For a large site, the site network has a complex structure and complex network facilities (for example, Layer 3 core devices). Therefore, the egress routers must support direct connection or dual-homing to Layer 3 devices. BGP, OSPF, and static routing are supported.
In the Layer 3 interconnection scenario, if only one CPE is deployed at a site, only a routing protocol needs to be configured on the LAN side based on requirements of LAN-side devices. If a CPE needs to interconnect with two LAN-side devices, the LAN-side devices must be stacked to function as a whole.

## Slide 36: Dual-Gateway Networking Scenario
Traffic routing for a dual-gateway site
    Two CPEs are deployed at a branch site as gateways, and each gateway has at least one WAN link, such as an MPLS or Internet link.
    In this deployment model, to support application-based traffic steering and ensure reliability, the two CPEs need to be considered as a whole so that users' service traffic can be routed across the CPEs.
    When LAN-side services need to access a remote site, the local site can select one from the two WAN links through the interlink between the CPEs.
    CPE1 can not only check the local link status, but also check the link status and SLA status of CPE2. In this way, CPE1 can select a WAN link based on a pre-configured application-based traffic steering policy.
LAN
MPLS
Internet
Site A
CPE1
CPE2
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 37: Dual-Gateway Interlink Solution
Edge CPE1
Edge CPE2
GE1/0/1
GE1/0/1
OSPF
GE1/0/3
GE1/0/3
Underlay
VRF
Overlay
VRF
Underlay
VRF
Overlay
VRF
Overlay tunnel
Overlay tunnel
Interlink
Dual-gateway design
    In the SD-WAN Solution, services are processed on a per-site basis, and the links on the two gateways (CPEs) at a site are regarded as a whole and all participate in traffic steering.
Interlink design
    The two gateways establish an interlink with each other through interconnection interfaces and forward service (VPN) traffic between them through sub-interfaces.
    Information, such as OSPF routing information, is synchronized between the gateways through interlink sub-interfaces.
WAN-side Networking
LAN-side Networking
Dual-Gateway

## Slide 38: Interfaces Connecting the Two Gateways
Single-link interconnection: Specify interfaces on the CPEs for interconnecting with each other.
Eth-Trunk interconnection: Specify two interfaces on each CPE for interconnecting with each other. The system automatically bundles the two interfaces into an Eth-Trunk.
For a dual-gateway site, configure a Layer 3 or Layer 2 link for interconnection between the two CPEs (gateways). By default, a Layer 3 link is used.
If only one interface is specified on each CPE, the two CPEs are interconnected with each other through a single link. If two interfaces are specified on each CPE, the system automatically binds the two interfaces into an Eth-Trunk, and the two CPEs communicate with each other through VLANIF interfaces.
A LAN-side Layer 2 link is used as the data forwarding channel between the CPEs. Data between the CPEs and data from the LAN side to the CPEs are isolated through VLANs, without affecting each other.
VLAN 4000
VLAN 4000
VLAN 4000
VLAN 4000
WAN-side Networking
LAN-side Networking
Dual-Gateway
Notes: To improve the reliability of egress links, multiple links are usually provided, that is, one active link and one standby link are used. This design is simple and reliable. The standby link is in backup state and does not forward network traffic in normal cases. Therefore, enterprise customers need to pay extra fees for reliability.
The SD-WAN Solution provides link backup. In this solution, multiple uplinks of a site are active at the same time and services can be load balanced among the links according to a preconfigured traffic scheduling policy. If a link is faulty, the link fault or quality deterioration can be detected within sub-seconds. Then, services can be switched from the faulty link to an operational link. This mechanism ensures link reliability and makes full use of enterprises' link resources, providing high access bandwidth and facilitating interconnection between enterprise sites.

## Slide 39
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
SD-WAN Networking Design
  Site Design
  Overlay Network Design
  Network Service Design

## Slide 40: RR Deployment Modes
Combined deployment of a site and RR
Independent deployment of RRs
Deployment of RRs in different areas
CPE
Branch 1
CPE
Branch 2
CPE (RR)
HQ/DC
CPE
Branch 1
CPE
Branch 2
CPE
HQ
RR
DC
Area C
RR
RR
RR
RR
Area D
Area A
Area B
RR Design
Overlay Planning
Topology Design
A site that functions as an RR not only undertakes tasks on the control plane but also forwards service traffic of other sites on the forwarding plane.
A site that functions as an RR does not have a LAN network, does not function as a hub for communication between other sites, and does not transmit service data. Such a site just undertakes tasks on the control plane.
At least one pair of RRs is deployed in each area. RRs in different areas establish BGP EVPN peer relationships with each other to advertise and learn VPN routes in different areas.

## Slide 41: RR Deployment Scenario: Enterprise-built Network
Independent deployment of RRs
Combined deployment of a site and RR
CPE
Branch 1
CPE
Branch 2
CPE (RR)
HQ/DC
CPE
Branch 1
Branch 2
CPE
HQ
RR
DC
Branch n
...
For small and midsize enterprises with a small number of branch sites and no heavy traffic between branches and the HQ/DC, it is recommended that the hub sites function as RRs and undertake tasks on the control plane.
For large-scale enterprises with a large number of sites and high network reliability requirements, it is recommended that the RRs be deployed independently.
RR Design
Overlay Planning
Topology Design

## Slide 42: RR Deployment Scenario: Carrier/MSP Resale Scenario
CPE
Branch 1
CPE
Branch 2
CPE
HQ/DC
Carrier/MSP DC
Enterprise A
CPE
Branch 1
CPE
Branch 2
CPE
HQ/DC
Enterprise B
Access area 1
Access area 2
RR
Deployment of MSP RRs
    In carrier/MSP resale scenarios, it is recommended that RRs be deployed independently. An MSP administrator creates RRs, divides access areas, and allocates the RRs to the corresponding access areas.
MSP RR shared by multiple tenants
    For small and midsize enterprises with a small number of sites, multiple tenants share one RR. Sites of different enterprise tenants are connected to the same multi-tenant RR, and the RR undertakes tasks on the control plane.
Independent allocation of MSP RRs
    For large enterprises with a large number of sites, RRs can be allocated independently. MSPs allocate RRs in access areas to the enterprises.
Deployment of tenant RRs
    For new enterprise customers, if the live network is a carrier's private line network and the carrier/MSP DC is unreachable, the hub site of a tenant can act as an RR.
RR Design
Overlay Planning
Topology Design

## Slide 43: Overlay Network Planning and Connection Management
Site B
Site A
TN | RD
MPLS-A | RD1
Internet-A | RD2
Site B
Internet-A
Internet-B
Site A
Internet-A
MPLS-A
Site B
Internet-A
Internet-B
Site A
TNs are in different RDs.
TNs are in the same RD.
TNs are physically interconnected in different RDs.
TN | RD
Internet-A | RD1
Internet-B | RD1
TN | RD
Internet-A | RD1
Internet-B | RD2
Sites A and B are interconnected with each other through two interconnected TNs on the underlay network. Two TNs are planned to be in the same RD and the two sites are interconnected with each other in full-mesh mode.
Sites A and B are interconnected with each other through two isolated TNs on the underlay network. Two TNs are planned to be in different RDs and the two sites establish two tunnels with each other.
Sites A and B are interconnected with each other through two interconnected TNs on the underlay network. Two TNs are planned to be in different RDs and the two sites establish two tunnels with each other.
RR Design
Overlay Planning
Topology Design

## Slide 44: Reliability Comparison Between Overlay RD Planning Modes
Site B
Internet-A
Internet-B
Site A
Site B
Internet-A
Internet-B
Site A
Fault scenario A
Fault scenario B
Site B
Internet-A
Internet-B
Site A
Site B
Internet-A
Internet-B
Site A
Fault scenario A
Fault scenario B
Physically interconnected TNs, different RDs
Same RD, different TNs
Different TNs in the same RD: higher networking reliability, but more virtual connection resources consumed
RR Design
Overlay Planning
Topology Design
Different TNs in different RDs: smaller number of connections and larger networking scale, but lower networking reliability

## Slide 45: Overlay Topology Design
Hierarchical networking
Partial-mesh networking
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Site1
Site2
Site3
Site4
HQ/DC
Border1
Border2
Full-mesh networking
Hub-spoke networking
RR Design
Overlay Planning
Topology Design
Notes: Hub-spoke networking
  The HQ or DC of an enterprise functions as a hub site, and enterprise branches function as spoke sites and access servers deployed at the HQ or DC through WANs.
Full-mesh networking
  Different branches of an enterprise can directly communicate with each other, without the need to divert traffic through intermediate nodes.
Partial-mesh networking
  A partial-mesh network can be considered as a type of special full-mesh network. If direct underlay network connections are available between two sites, traffic is directly transmitted between the sites. Otherwise, traffic between the sites is forwarded through a redirect site, to which both sites are connected.
Hierarchical networking
  The hierarchical network model can be considered as a combination of single-layer network models. A WAN is divided into multiple areas, which are interconnected through a centralized backbone area. In this way, sites can communicate with each other across areas.

## Slide 46: Hub-Spoke Networking Scenario
Spoke
Branch 1
Branch 2
Hub
HQ/DC
Solution description
  The HQ or DC of an enterprise functions as a hub site, and enterprise branches function as spoke sites and access servers deployed at the HQ or DC through WANs.
  If enterprise branches need to communicate with each other, traffic needs to be forwarded by the hub site. External traffic of all branch sites must be first sent to the hub site.
Application scenarios
  Enterprises whose major service traffic is sent from branch sites to hub sites and applications are centrally stored on servers at the HQ and DC sites
  Enterprises with almost no traffic transmitted between branch sites, for example, chain enterprises. The major service traffic of chain enterprises is sent from chain branches to the HQ or DC, and there is almost no traffic between chain branches.
RR Design
Overlay Planning
Topology Design

## Slide 47: Dual-Hub Active-Active Networking Scenario
Spoke
Branch1
Branch2
Hub1
DC1
Hub2
DC2
DCI
Production service
Office service
Production service
Office service
Spoke
Branch1
Branch2
Hub1
DC1
Hub2
DC2
DCI
Area 1
Area 2
Spoke
Scenario 2: active-active hub sites based on spoke sites
Scenario 1: active-active hub sites based on service network segments
Hub1 is the primary hub site for office services.
Hub2 is the primary hub site for production services.
Hub1 is the primary hub site for Area1.
Hub 2 is the primary hub site for Area2.
Primary path
Backup path
Primary path
Backup path
RR Design
Overlay Planning
Topology Design

## Slide 48: Full-Mesh Networking Scenario
Edge
Branch1
Branch2
Edge
HQ/DC
Solution description
  Different branches can directly communicate with each other, without the need to divert traffic through intermediate nodes.
Application scenarios
  Small enterprises with a small number of sites or large enterprises whose branches need to communicate with each other
  Large enterprises with collaborative services (for example, high-value applications such as VoIP and video conferencing). These services have high requirements on network performance such as the packet loss rate, latency, and jitter, and require direct communication between branch sites.
  The full-mesh networking is simple and features high service access efficiency but average scalability. It is applicable to networks with 10 to 100 branch sites.
RR Design
Overlay Planning
Topology Design

## Slide 49: Partial-Mesh Networking Scenario
Edge
Branch1
Branch2
Edge (Redirect)
HQ/DC
Branch3
Solution description
  A partial-mesh network can be considered as a type of special full-mesh network. If direct underlay network connections are available between two sites, traffic is directly transmitted between the sites. Otherwise, traffic between the sites is forwarded through a redirect site, to which both sites are connected.
Application scenarios
  The underlay networks of the sites that need to directly communicate with each other cannot be directly interconnected. In this case, the sites can communicate with each other through the redirect site.
  In the full-mesh networking scenario, the underlay networks of the sites that need to directly communicate with each other can be directly interconnected. For reliability purposes, a redirect site is deployed. In this manner, when the underlay networks of the sites are faulty and the sites cannot directly communicate with each other, traffic of the sites can be forwarded by the redirect site.
RR Design
Overlay Planning
Topology Design

## Slide 50: Hierarchical Networking Scenario
Solution description
  The hierarchical network model can be considered as a combination of single-layer network models. A WAN is divided into multiple areas, which are interconnected through a centralized backbone area. In this way, a large number of sites can communicate with each other across areas.
  For example, the network of a multinational enterprise is divided into three areas (China, Europe, and America) based on the enterprise's management structure. Each area uses a single-layer network topology (hub-spoke or full-mesh) with one or more sites as border sites. The border sites constitute the backbone area (level-1 backbone network), which implements interconnection of the areas. Border sites of an area are connected to both the level-2 area network and level-1 backbone network.
Application scenarios
  The hierarchical network model features a clear network structure and excellent scalability, and is therefore applicable to enterprises with a large number of sites or multinational enterprises with widely distributed sites.
MPLS
Internet
MPLS
Internet
MPLS
Internet
Level-1 network
Level-2 network
RR Design
Overlay Planning
Topology Design

## Slide 51
Basic Concepts of SD-WAN Networking
Understanding SD-WAN Flexible Networking
SD-WAN Networking Design
  Site Design
  Overlay Network Design
  Network Service Design

## Slide 52: Internet Access Solution
The SD-WAN Solution involves the following Internet access scenarios:
  Local Internet access
  Centralized Internet access
  Hybrid Internet access
Branch3
Branch2
HQ
Branch1
Legacy site
NAT
Local Internet access
Centralized Internet access
Network controller
Notes: Local Internet access
  Internet access traffic of a site is directly routed out from local CPEs.
Centralized Internet access
  Internet access traffic of all sites is diverted to the centralized Internet access site and then to the Internet.
Hybrid Internet access
  Local Internet access + centralized Internet access for all traffic: By default, all Internet access traffic is routed out through the local Internet access interface. If the local Internet access interface is faulty, Internet access traffic is diverted to the centralized Internet access site and then to the Internet.
  Centralized Internet access + local Internet access (for specified traffic): By default, Internet access traffic is routed out through the centralized Internet access site. Traffic of some specified services (for example, Office365) is directly routed out through local WAN links.
Note: When users in multiple departments access the Internet at the same time, ensure that the users' IP addresses in different departments do not overlap.

## Slide 53: Local Internet Access
Solution description
Internet access traffic of a site is routed out from the local Internet link.
Local Internet access policies can be configured on a per-department or per-site basis.
Local Internet access can be implemented in either of the following modes based on traffic classification:
  All Internet access traffic is routed out from the local site.
  Only Internet access traffic of specified applications is routed out from the local site.
Outbound interfaces must be configured for local Internet access. A maximum of three outbound interfaces can be configured. If multiple outbound interfaces are configured, Internet access link backup is implemented based on the priorities of the outbound interfaces.
In local Internet access mode, NAT is provided. You can determine whether to enable the NAT function based on the outbound interface. Currently, NAT in Easy IP mode is provided. That is, the IP address of the outbound interface is used as the post-NAT public IP address.
Internet
CPE2
CPE1
Branch
Branch
MPLS
IGW
Application scenarios
Local Internet access is applicable to small-scale enterprises or scenarios where Internet access traffic does not require centralized security control and links for accessing the Internet are available on the WAN side.
Notes: Internet access traffic cannot be load balanced among multiple links. Only priority-based link backup is supported.
Local Internet access for specified applications must be enabled together with centralized Internet access, and is implemented through policy-based routing (PBR).
When local Internet access is enabled, the default routes on the underlay WAN need to be configured separately. The default routes can be static routes (for Internet access through Internet interfaces) or BGP/OSPF routes (for Internet access through MPLS network interfaces).

## Slide 54: Centralized Internet Access
Internet
CPE2
CPE1
Branch
HQ (centralized Internet access site)
MPLS
Solution description
Internet access traffic of all sites of a tenant is routed out through a centralized Internet access site.
The centralized Internet access site can use either of the following methods for Internet access:
  The site has an Internet egress on the LAN side, through which all Internet access traffic is routed out. In this case, you need to configure default routes on the LAN side, or configure a dynamic routing protocol so that the default routes can be learned from the LAN side.
  The site can also access the Internet through WAN-side interfaces, through which all Internet access traffic is routed out. (Note that local Internet access must be enabled for the centralized Internet access site.)
Application scenarios
Centralized Internet access is applicable to scenarios where sites do not have links for accessing the Internet or Internet access traffic requires centralized security control. In this mode, a centralized Internet access gateway is configured. Traffic from other sites is forwarded to the centralized Internet gateway through the overlay network and then to the Internet.

## Slide 55: Hybrid Internet Access: Local Internet Access (Default) + Centralized Internet Access (Backup)
Internet
CPE2
CPE1
Branch
HQ
MPLS
Solution description
Both local Internet access and centralized Internet access are enabled on the SD-WAN network.
All Internet access traffic of sites is routed out through local WAN-side links.
If a site has one local Internet access path and one centralized Internet access path, the default priority of the local Internet access path is higher.
By default, all Internet access traffic is routed out through the local Internet access interface. If the local Internet access interface is faulty, Internet access traffic is diverted to the centralized Internet gateway and then to the Internet.
Application scenarios
This Internet access mode is applicable to small-scale enterprises or scenarios where Internet access traffic does not require centralized security control, sites have WAN-side links for accessing the Internet, and high Internet access reliability is required.

## Slide 56: Hybrid Internet Access: Centralized Internet Access (Default) + Local Internet Access (for Specified Applications)
Internet
CPE2
CPE1
Branch
HQ
MPLS
Solution description
Both local Internet access and centralized Internet access are enabled on the SD-WAN network.
At the centralized Internet access site, local Internet access is enabled and all Internet access traffic is routed out from this site.
At other sites, local Internet access is enabled and Internet access traffic of specified applications is routed out from the local site.
If a site has one local Internet access path and one centralized Internet access path, the default priority of the local Internet access path is higher.
By default, Internet access traffic is routed out through the centralized Internet access site. Internet access traffic of specified experience-sensitive applications is routed out through local WAN-side links.
Application scenarios
This Internet access mode is applicable to the scenarios where a site has links for accessing the Internet, most Internet access traffic requires centralized security control, and Internet access traffic of some applications can be routed out from the local site according to SLA requirements.

## Slide 57: Internet Access Link Reliability
Backup link solution design
  Site-to-Internet access is configured by site. A maximum of three WAN links can be configured for each site as the site-to-Internet links.
  Each WAN link has a unique priority when it functions as a site-to-Internet link. That is, only one WAN link can function as the active site-to-Internet link at a time.
  If the WAN link with the highest priority is faulty, site-to-Internet traffic is automatically switched to the link with the second highest priority.
  The backup link and hybrid Internet access can be enabled at the same time.
Internet3
CPE2
Branch
Internet2
Internet1
Priority = 1
Priority = 2
Priority = 3

## Slide 58
(Multiple choices) Which of the following parameters are required for establishing a control tunnel in the SD-WAN Solution?
  TNP
  IPsec SA
  Service route
  Loopback interface of the CPE or RR
Notes: 1. ABCD

## Slide 59
SD-WAN flexible networking involves three steps:
  Management channel establishment, control channel establishment, and data channel establishment
The overlay topology can be controlled by controlling the next hop of service routes on the RR.
If a NAT device is deployed on a network, CPEs can use STUN technology to establish data channels with each other traversing the NAT device.
SD-WAN supports both single-CPE and dual-CPE networking modes.
SD-WAN supports four topology types:
  Hub-spoke, full-mesh, partial-mesh, and hierarchical topologies
SD-WAN supports three Internet access modes:
  Local Internet access, centralized Internet access, and hybrid Internet access