## Slide 1
V5R02
V1R1
Huang Weihong/00374839
2020.02.29
He Junjian/WX580230
Update
2019.01.25
Update
2019.01.25
Update
2019.01.25
Update
2019.01.25
Update
2019.01.25
Update

## Slide 2: SD-WAN Application Experience

## Slide 3
Enterprises generally deploy diversified types of applications, which have different requirements on bandwidth and link quality. For example, real-time video conferencing has low tolerance for packet loss, delay, and jitter of links. If packet loss occurs on links, frame freezing and artifacts occur. The applications such as email and FTP-based file transfer are relatively insensitive to packet loss but require high bandwidth to ensure quick transfer.
To meet diversified requirements of applications, traditional WANs have the following issues to resolve:
  Applications of different values are carried on the same link.
  When link quality deteriorates, dynamic traffic steering cannot be implemented.
  No effective measure is available when the link quality deteriorates.
To resolve these issues, Huawei SD-WAN Solution provides experience assurance for enterprise applications.
This course describes SD-WAN application experience assurance, involving application-based traffic steering, hierarchical quality of service (HQoS), and WAN optimization.
Notes: This course is based on Huawei SD-WAN Solution.

## Slide 4
On completion of this course, you will be able to:
  Describe the overall application experience implementation process.
  Describe benefits of link quality measurement (LQM).
  Describe application scenarios of HQoS.
  Differentiate traffic steering policies.

## Slide 5
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
HQoS
WAN Optimization

## Slide 6: Application Experience Solution Overview
Huawei SD-WAN application experience solution consists of four parts:
  Application identification: identifies the enterprise applications to which network traffic belongs based on traffic characteristics.
  Application-based traffic steering: continuously monitors the status of multiple WAN links based on link quality requirements of enterprise applications, and selects the optimal link for traffic transmission.
  HQoS: provides differentiated services for diversified enterprise applications based on QoS. In addition, HQoS provides service quality guarantee by service, department, and site.
  WAN optimization: Packet loss compensation technology prevents frame freezing and artifacts of videos even if the link quality deteriorates and a large number of packets are lost. In addition, transmission and data optimization technologies are provided to improve data transmission efficiency.
Application identification
First packet identification (FPI)
Feature identification
Application identification process
Application-based traffic steering
HQoS
HQoS process
Enterprise scenario: HQoS
WAN optimization
Application scenarios of packet loss optimization
FEC/A-FEC
FEC/A-FEC implementation
Link quality measurement (LQM)
Application quality measurement (AQM)
Intelligent traffic steering algorithms
FEC: forward error correction
A-FEC: adaptive FEC

## Slide 7
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
  Overview of Application Identification and Intelligent Traffic Steering
  LQM
  AQM
  Intelligent Traffic Steering Algorithms
HQoS
WAN Optimization

## Slide 8: Application Identification and Traffic Steering
Huawei SD-WAN Solution uses Smart Application Control (SAC) technology to implement application identification and Smart Policy Routing (SPR) technology to implement application-based traffic steering.
  SAC enables a device to identify applications and group traffic based on the service awareness (SA) and FPI signature databases.
  SPR enables a device to determine the link quality based on link detection packets and then select the traffic forwarding path.
MPLS
Internet
Video applications
Internet access service
Voice applications
SAC module
Application identification
Application-based traffic steering
1
2
SPR module
Link detection
Link detection
Application identification and traffic steering processes
Notes: For details about SAC and SRP, see HA Technologies.

## Slide 9: Intelligent Traffic Steering Overview: Key Technologies
Identification result
Session table
IP address prefix
NHP
SPR
SAC signature database
Application identification
Identified original packets
Overlay tunnel
Underlay
SA signature database
URL identification
FPI
Packet
Send
Application identification
Application-based traffic steering
Overlay tunnel encapsulation
Link quality
Application requirements
Notes: After receiving a service packet, a CPE processes the packet as follows:
  Identifies the application.
    If no session table exists, the CPE identifies the service type of the packet based on the SA signature database, URL identification, or FPI, performs application-based traffic steering, and sets up a session table.
    If a session table exists, the CPE directly performs application-based traffic steering.
  Performs application-based traffic steering.
    If intelligent traffic steering is not configured, the CPE searches the routing table for a route to forward the packet.
    If an intelligent traffic steering policy is configured, the CPE performs traffic steering based on the link or application quality.
  Finally, the CPE performs overlay and underlay tunnel encapsulation for the packet, and sends it out.

## Slide 10: SAC Application Identification Process
During SAC application identification, a network device checks whether an application is identified. If not, the network device matches the application against the FPI signature database and SA signature database in sequence.
Network device
FPI signature database
Service traffic
Signature matching
SA signature database
Signature matching
Application identification record
SAC detection
Traffic of identified applications is directly forwarded at Layer 3.
Voice
Video
Web page
Download
Forwarding table
Notes: For details about application identification, see HA Technologies.

## Slide 11: What Is Intelligent Traffic Steering?
Intelligent traffic steering monitors link quality in real time based on application requirements and then selects the optimal link for traffic transmission.
Different applications have different service level agreement (SLA) requirements. Intelligent traffic steering can be deployed to dynamically and automatically select network paths that meet applications' SLA requirements among multiple WAN links with different network quality, while ensuring WAN network efficiency.
HQ
LTE best-effort link
Internet
MPLS
Video, voice
Data
Branch

## Slide 12
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
  Overview of Application Identification and Intelligent Traffic Steering
  LQM
  AQM
  Intelligent Traffic Steering Algorithms
HQoS
WAN Optimization

## Slide 13: LQM
LQM is the basis of application-based traffic steering and relies on the keepalive mechanism.
Keepalive interaction is implemented between a primary device and a secondary device. The primary device automatically sends keepalive request packets based on a timer to control sessions. The secondary device only needs to respond to the keepalive request packets.
keepalive interaction is unidirectional. After the primary device receives the instruction of enabling detection delivered by the controller, it constructs and encapsulates packets and the timer is triggered for sending packets.
The primary and secondary devices are negotiated based on the following rules:
  An RR does not function as the primary device.
  An IWG does not function as the primary device.
  The device with a smaller site ID functions as the primary device.
Site A
Site B
IPsec VPN tunnel
Primary
Secondary
Internet/MPLS
Send a keepalive request packet,
seq=n...
Reply with a keepalive ACK packet,
seq=n...

## Slide 14: Keepalive Detection Mechanism
Site A
Send keepalive detection packets.
Respond to the keepalive detection packets.
Keepalive detection action taken by the primary device
  By default, the primary device sends a keepalive detection packet every 1000 ms for six times in a detection period.
  If the primary device does not receive any keepalive response packet from the secondary device within 6 seconds, keepalive detection fails.
  The default keepalive detection parameters can be modified on iMaster NCE-WAN.
Keepalive detection action taken by the secondary device
  After receiving a keepalive detection packet, the secondary device responds immediately.
  If the secondary device does not receive any keepalive detection packet within a detection period, keepalive detection fails.
Site B
Delay
Jitter
Packet loss rate

## Slide 15: Viewing LQM Information on iMaster NCE-WAN
LQM
  The LQM of a link is calculated based on the packet loss rate, delay, and jitter. The LQM is calculated as follows by default:
    LQM = F (Delay) x Weight (25%) + F (Jitter) x Weight (25%) + F (Packet loss rate) x Weight (50%)
  The parameters in the LQM calculation formula can be modified.
  The LQM of a site is the average of the LQM values of all links at the site.
  The LQM between sites is the average of the LQM values of all links between the sites.

## Slide 16: Viewing the Site Health on iMaster NCE-WAN
Site health calculation method
  Single-gateway site:
    Site health score = Site LQM x 10 x 0.1 + Gateway health score x 0.9
  Dual-gateway site:
    Site health score = Site LQM x 10 x 0.1 + (Health score of gateway 1 + Health score of gateway 2) x 0.9∕2
Note: The health score of a gateway is obtained by calculating the CPU usage and memory usage.

## Slide 17
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
  Overview of Application Identification and Intelligent Traffic Steering
  LQM
  AQM
  Intelligent Traffic Steering Algorithms
HQoS
WAN Optimization

## Slide 18: AQM Implementation
When an application client sends a connection request to an application server through a router, the router forwards the request to the application server, identifies the SYN packet in the first handshake, obtains the source and destination IP addresses, creates a bidirectional flow table, and records the timestamp.
After the application server receives the connection request, the router identifies the SYN-ACK packet in the second handshake by querying the flow table, records the timestamp, forwards the response packet sent by the application server to the application client, and calculates the network delay of the application server (TCP_SND).
When the response packet reaches the application client, the router identifies the ACK packet in the third handshake by querying the flow table, records the timestamp, and calculates the network delay of the application client (TCP_CND).
DATA_SND: response delay, that is, the difference between the time when the client sends a connection request and the time when the first response packet is received
Packet loss rate = Number of retransmitted packets/Total number of sent packets
Application client providing applications for users
Application server providing services for application clients
SYN
SYN-ACK
ACK
TCP_SND
TCP_CND
Request1
Data1
DATA_SND
AD
Client
Router
Server
Delay
Packet loss rate

## Slide 19: Viewing AQM Information on iMaster NCE-WAN
AQM
  The AQM is calculated based on the packet loss rate and delay of an application.
  By default, AQM = F (Delay) x Weight (50%) + F (Packet loss rate) x Weight (50%)
  The parameters in the AQM calculation formula can be modified.

## Slide 20
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
  Overview of Application Identification and Intelligent Traffic Steering
  LQM
  AQM
  Intelligent Traffic Steering Algorithms
HQoS
WAN Optimization

## Slide 21: Intelligent Traffic Steering Algorithms
Category | Traffic Steering Algorithm | Description | Mandatory or Optional
Basic traffic steering | Link quality–based traffic steering | Traffic steering is implemented based on link quality. If the quality of one link does not meet SLA requirements (including the delay, jitter, and packet loss rate), a link switchover is triggered. If one of the switchover conditions (delay, jitter, and packet loss rate) exceeds the specified threshold, a link switchover is triggered. The system pre-defines the thresholds of the switchover conditions for four typical services: voice, real-time video, low-delay data, and large-volume data services. You can directly select a specific service type to implement traffic steering. You can also customize the thresholds of the switchover conditions based on service requirements. | Mandatory
Advanced traffic steering | Bandwidth-based traffic steering | You can set the upper and lower thresholds for the link bandwidth utilization to implement bandwidth-based traffic steering. If the link bandwidth utilization is less than the lower threshold, the existing and subsequent traffic is forwarded over the current transport network. If the link bandwidth utilization is between the lower and upper thresholds, the existing traffic is still forwarded over the current transport network, and subsequent traffic is switched to another transport network. If the link bandwidth utilization is greater than the upper threshold, some existing traffic and all subsequent traffic are switched to another transport network. | Optional
 | Load balancing–based traffic steering | When there are multiple links, per-flow load balancing can be performed for application traffic over these links. | Optional
 | Application priority–based traffic steering | If multiple types of service packets are transmitted on the same link, traffic of high-priority applications is preferentially processed when congestion occurs, delivering optimal user experience. | Optional
Notes: Each site can be configured with primary and secondary transport networks.
  Primary transport network: You can configure multiple primary transport networks for a site and specify priorities of them. A smaller value indicates a higher priority. You can set the same priority for multiple primary transport networks.
  Secondary transport network: A secondary transport network provides escape links. Application traffic is switched to a secondary transport network only when all the primary transport networks are unavailable.

## Slide 22: Intelligent Traffic Steering Algorithm: Link Quality-based Traffic Steering
Traffic steering is implemented based on link quality. If the quality of one link does not meet SLA requirements (including the delay, jitter, and packet loss rate), a link switchover is triggered.
If one of the switchover conditions (delay, jitter, and packet loss rate) exceeds the specified threshold, a link switchover is triggered.
Application scenario: Different applications have different SLA requirements for links. When a link does not meet the SLA requirements, traffic needs to be dynamically switched to another link that meets the SLA requirements.
5
4
3
2
1
CPE
CPE
CPE
CPE
5
4
Good-quality link
Voice services have low tolerance for the delay and packet loss rate. A CPE performs periodic link detection to monitor the delay, jitter, and packet loss rate of a link in real time, over which application traffic is transmitted. If one of the three switchover conditions exceeds the specified threshold, a link switchover is triggered.
Before a link switchover
After a link switchover
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering
3
2
1

## Slide 23: intelligent traffic steering Algorithm: Link Quality-based Traffic Steering Configuration
Select Voice.
Set a higher priority for the MPLS network than the Internet.
Policy priority
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering

## Slide 24: Intelligent Traffic Steering Algorithm: Bandwidth-based Traffic Steering
When the bandwidth of a link reaches a given threshold or its remaining bandwidth is lower than a given threshold, the link cannot be selected for forwarding subsequent traffic of certain applications, so as to prevent application or link quality deterioration.
The link bandwidth of high-priority applications is preferentially guaranteed. To prevent high-priority applications from occupying all the link bandwidth, you can configure bandwidth limits for the applications. In this way, when the bandwidth utilization of an application reaches a given threshold, subsequent traffic of the application will be switched to another link.
Application scenarios: Bandwidth resources are reserved for high-priority applications to ensure their user experience while high-value links are fully utilized.
4
3
2
1
CPE
CPE
CPE
CPE
2
1
VoIP data flow 1
2
1
6
5
4
3
4
3
VoIP data flow 2
As the bandwidth utilization of one link increases, VoIP data flow 2 is transmitted over another link.
2
1
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering
Notes: MPLS links are high-value links, which are expected to be fully utilized. To ensure user experience of high-priority applications, it is recommended that MPLS links not be used to transmit traffic of low-priority applications when the link bandwidth utilization exceeds 70%.
A link cannot be selected for bandwidth-demanding services (such as the backup service) when its remaining bandwidth is insufficient. In this case, bandwidth-based traffic steering can be configured.
For example, an enterprise leases MPLS, Internet1, and Internet2 links. It expects to reserve certain bandwidth resources for high-value VoIP services to ensure user experience of VoIP services, while fully utilizing the MPLS link. In this case, bandwidth-based traffic steering can be configured. In addition, bandwidth conditions can be configured for low-value applications (such as email and FTP services) to select the MPLS link. For example, when the bandwidth utilization of the MPLS link exceeds 50%, new traffic is not transmitted over the MPLS link; when the bandwidth utilization of the MPLS link exceeds 70%, existing traffic on the MPLS link needs to dynamically switch to other links.

## Slide 25: Intelligent Traffic Steering Algorithm: Bandwidth-based Traffic Steering Configuration
Bandwidth-based traffic steering configurations for an FTP application group
Configure bandwidth conditions for different links.
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering
Notes: Bandwidth-based traffic steering is applicable to FTP applications, with an MPLS link as the primary link and an Internet link as the secondary link. When the bandwidth utilization of the MPLS link exceeds 50%, a primary/secondary link switchover is triggered.
Bandwidth-based traffic steering is not applicable to VoIP services. VoIP services use an MPLS link as the primary link and an Internet link as a secondary link.

## Slide 26: Intelligent Traffic Steering Algorithm: Load Balancing-based Traffic Steering
When load balancing–based traffic steering is deployed, per-flow load balancing can be performed among multiple links with the same priority. Bandwidth proportion–based load balancing can be performed among multiple links that have the same priority and meet SLA requirements.
Application scenarios: When an enterprise has multiple links and expects to fully utilize the link bandwidth, load balancing–based traffic steering can be deployed.
4
3
2
1
CPE
CPE
VoIP data flow 1
4
3
VoIP data flow 3
2
1
4
3
2
1
VoIP data flow 2
As shown in the figure above, an enterprise purchases two MPLS links (one with the 100 Mbit/s rate and the other with the 50 Mbit/s rate) from different carriers, which can be added to the primary link group of the VoIP service. If the quality of both links meets the SLA requirements of the VoIP service, VoIP service flows can be carried over the two MPLS links in load balancing mode. Through real-time bandwidth utilization monitoring, the bandwidth utilization can be higher than 85%, ensuring full bandwidth utilization of the links.
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering

## Slide 27: Intelligent Traffic Steering Algorithm: Load Balancing-based Traffic Steering Configuration
Select Load balance.
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering

## Slide 28: Intelligent Traffic Steering Algorithm: Application Priority-based Traffic Steering
For example, an enterprise leases an MPLS link and an Internet link from a carrier, and expects to fully utilize the MPLS link. To achieve this, the enterprise sets highest priorities for high-value applications and lower priorities for low-value applications (such as email and FTP applications). In addition, the enterprise sets the MPLS link as the primary link and the Internet link as the secondary link. In this way, when the MPLS link is congested, the CPE preferentially schedules traffic of low-priority applications to the Internet link based on application priorities to prevent quality deterioration of the MPLS link from affecting high-value applications.
Application scenarios: High-value links (such as MPLS links) need to be preferentially selected and fully utilized. When link congestion occurs, traffic of low-priority applications needs to be preferentially scheduled to low-value links (such as Internet links).
5
4
3
2
1
CPE
CPE
5
4
3
2
1
7
6
5
4
CPE
CPE
7
6
5
4
VoIP data flow
FTP data flow
3
2
1
3
2
1
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering

## Slide 29: Intelligent Traffic Steering Algorithm: Application Priority-based Traffic Steering Configuration (VoIP)
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering
Voice

## Slide 30: Intelligent Traffic Steering Algorithm: Application Priority-based Traffic Steering Configuration (FTP)
Bulk Data
Lowest priority
Link Quality–based Traffic Steering
Bandwidth-based Traffic Steering
Load Balancing–based Traffic Steering
Application Priority–based Traffic Steering

## Slide 31: Intelligent Traffic Steering Implementation: Action Taken When SLA Requirements Are Not Met
If no link on the primary transport network meets SLA requirements or the link bandwidth utilization exceeds a given threshold, traffic steering is performed in the following modes:
  Random link selection: When Inter-TN Policy is set to Prefer, a relatively optimal link is selected among the links on the primary transport network.
  ECMP: When Inter-TN Policy is set to Load balance, the CPE searches the routing table for a route to forward packets.
  Discard: If an escape link is configured, packets are forwarded through the escape link. If no escape link is configured, all packets are discarded, which may cause service interruption.
Random link selection
4 | 3 | 2 | 1
4 | 3 | 2 | 1
Discard
4 | 3 | 2 | 1
4 | 3 | 2 | 1
If no escape link is configured, all packets are discarded.
Primary link 1
Primary link 2
A relatively optimal link is selected.

## Slide 32: Intelligent Traffic Steering Implementation: Link Switchback
The Switchover mode parameter specifies whether to allow traffic to switch back to the original link if the quality of the original link recovers. Link switchovers include the switchover between primary transport networks with different priorities and the switchover between primary and secondary transport networks.
Link switchover
4 | 3 | 2 | 1
4 | 3 | 2 | 1
Link switchback
4 | 3 | 2 | 1
4 | 3 | 2 | 1
Primary link 1
Primary link 2
4 | 3 | 2 | 1
4 | 3 | 2 | 1
When the quality of primary link 1 does not meet requirements, traffic is switched to primary link 2.
After the quality of primary link 1 recovers, traffic is switched back to primary link 1.

## Slide 33: Intelligent Traffic Steering Implementation: Scheduling Following
MPLS
The primary party sends packets.
When incoming and outgoing paths are inconsistent, the inbound link may become congested. The scheduling following function solves this problem. After the primary and secondary parties are determined based on certain rules and the primary party performs traffic steering, the secondary party follows the traffic steering result of the primary party.
The primary party is determined as follows:
  Between dual-gateway sites: The site with a smaller ID is selected as the primary party.
  Between a single-gateway site and a dual-gateway site: The single-gateway site is selected as the primary party.
  Between single-gateway sites: The site with a smaller WAN uplink bandwidth is selected as the primary party. If the sites have the same WAN uplink bandwidth, the site with a smaller ID is selected as the primary party.
  Between a tenant site and an IWG (POP): The tenant site is selected as the primary party.
Scenario | Primary Party | Secondary Party
1 | Selects the Internet link preferentially. | Selects the Internet link too.
2 | Switches traffic to the MPLS link when detecting that the inbound traffic rate of the Internet link exceeds a given threshold. | Switches traffic to the MPLS link too.
The secondary party forwards packets based on the traffic steering result of the primary party.
Internet
Notes: The scheduling following function is supported only when Inter-TN Policy is set to Load balance. Dynamic primary/secondary switchover is not supported.

## Slide 34
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
HQoS
WAN Optimization

## Slide 35: QoS Data Processing Procedure (DiffServ Model)
Video
Voice
Data
Inbound interface
Traffic classification
Token
bucket
Token
Re-marking
Other
processes
...
Queue 0
Queue 1
Queue 2
Queue N
...
GTS
WRED
Congestion avoidance
Entering queues
Scheduling
Congestion management
Traffic shaping
Traffic policing
Outbound interface
Leaving queues
CAR
Notes: QoS provides the following functions:
  Traffic classification and marking: helps to identify objects based on certain matching rules, which is the prerequisite for implementing differentiated services. Traffic classification and marking are typically applied to the inbound interface.
  Token bucket: is used to check whether traffic meets packet forwarding conditions.
  Traffic policing: monitors the volume of specific data traffic that arrives at a network device, and is typically applied to the inbound interface. When traffic exceeds a given amount, traffic limiting and punishment are performed to protect network resources and enterprise users' interests.
  Congestion avoidance: Severe congestion causes damage to network resources. The congestion avoidance mechanism enables a device to monitor the utilization of network resources, and discards packets when network congestion becomes worse, thus to regulate network traffic and prevent network overload. Congestion avoidance is typically applied to the outbound interface.
  Congestion management: must be implemented to solve the problem of resource competition. Packets are buffered in a queue and a scheduling algorithm is adopted to determine the packet forwarding sequence. Congestion management is typically applied to the outbound interface.

## Slide 36
Notes:   Traffic shaping: is a traffic control measure that initiatively adjusts the output speed of traffic. Traffic shaping enables traffic to adapt to the network resources that can be provided by downstream devices to prevent packet loss and congestion. Traffic shaping is typically applied to the outbound interface.

## Slide 37: HQoS Service Scenario: Enterprise Scenario
Objective: HQoS ensures that traffic of important applications, departments, and services is preferentially transmitted when the egress bandwidth purchased by an enterprise is limited.
  Different priorities are guaranteed for different applications.
  Different departments occupy different bandwidths.
  The Internet access traffic is limited within a proper range.
HQ
Branch site
Department 2
Voice, video, email
Department 1
Video, voice
Email, entertainment
HQoS on the outbound interface
Inter-site access traffic
Local Internet access traffic
Branch site
Legacy MPLS
site
Public cloud site
Internet
MPLS
POP/
Backbone network
CPE
CPE
CPE
IWG
vCPE
Gateway
Gateway

## Slide 38: Enterprise Scenario: HQoS
VPN 1
40%
Child policy
Parent policy
Parent policy bound to an interface
Multiple applications in a department
  Enterprise applications have different link requirements and different importance. The experience of important applications should be preferentially guaranteed when the egress link bandwidth is limited.
Multiple departments of an enterprise
  An enterprise usually has multiple departments of different importance, which require traffic isolation and differentiated bandwidths.
Solution:
  Different HQoS policies, such as queue scheduling, CAR, and traffic shaping, can be configured for each VPN based on applications.
  The minimum guaranteed bandwidth proportion can be specified for each VPN. This prevents some VPNs from preempting the bandwidth of other VPNs in the case of network congestion.
Overlay
60%
WAN interface
100 Mbit/s
VPN 2
60%
Overlay
70%
VoIP
Email
SaaS
VoIP
Email
SaaS
Service-level QoS
Overlay local Internet access traffic measurement
Interface-based rate limiting
Local Internet access
40%
Local Internet access
30%
Notes: An enterprise usually has multiple departments of different importance, which require traffic isolation and differentiated bandwidths.
  A specified bandwidth quota is assigned to each department to meet its service requirements.
  If some departments do not fully use their bandwidth quotas, idle bandwidth resources can be used by other departments with insufficient bandwidth.
  The bandwidth for Internet access or legacy site access needs to be limited separately.

## Slide 39: Enterprise Scenario: Intra-VPN HQoS Policy
High
Low
EF queue
BE queue
Interface
Video
Email
CPE
CPE
Video
Email
1
User 1
User 2
User 3
2
Link1
Link2
Traffic classifier
Traffic policy
Create traffic classifiers.
  When traffic of VPN users (for example, voice, data, office application, and Internet access traffic) needs to be classified, a traffic classifier must be created for each type of traffic object.
Internet
Configure actions in HQoS traffic policies.
  Create HQoS policies, select a corresponding traffic classifier for each policy, and specify the HQoS action to be taken for the traffic object corresponding to each policy.
Notes: Traffic can be classified based on one or a combination of the following:
  Five-tuple
  Applications or application groups
  DSCP values
Currently, the following traffic actions are supported:
  Priority-based queue scheduling
  Bandwidth limiting: CAR & shaping
  DSCP re-marking

## Slide 40
Application Experience Solution Overview
Application Identification and Intelligent Traffic Steering
HQoS
WAN Optimization

## Slide 41: Application Scenario of Packet Loss Optimization
Data center
MPLS
Internet
Video surveillance
Video surveillance
  Characteristics: from multiple sites to one site, one-way
  Key issue: Network packet loss affects video quality.
  Deployment locations: egresses of the camera area and data center
Video conferencing
  Characteristics: from multiple sites to one site, two-way
  Key issue: Network packet loss affects video quality.
  Deployment locations: egresses of the video terminal site and data center
Video conferencing
FEC is configured on iMaster NCE-WAN.
Video backhaul (UDP)
Two-way video transmission (UDP)
Packet loss
Packet loss
Client 1
Client 2
Data center
FEC is configured on iMaster NCE-WAN.
Video backhaul

## Slide 42: FEC/A-FEC
Scenario:
  An employee initiates a video conference at a branch site and connects to the data center. Because video conferencing is sensitive to packet loss and the traffic needs to go through the Internet that has poor quality, the packet loss and delay requirements cannot be met. As a result, the video quality deteriorates, and frame freezing and artifacts occur.
Solutions:
  FEC
  A-FEC
CPE
FEC
Data center
CPE
FEC
CPE
FEC
MPLS
Site A
Site B
Notes: FEC optimization technology is used to optimize packet loss by specifying data flows based on 5-tuple information through an agent. The agent obtains specified data flows, adds verification information to packets, and performs verification at the receive end. If a packet is lost or damaged on the network, it can be recovered based on the verification information.
On the basis of FEC, A-FEC can automatically adjust the FEC redundancy rate to save bandwidth when the packet loss rate is low. When the packet loss rate increases sharply in a short period of time, the redundancy rate can be increased adaptively to offset the impact of packet loss on the network.
Huawei FEC/A-FEC has the following advantages:
  Different from the TCP-based retransmission mechanism, FEC does not require packet retransmission and has high real-time performance.
  Compared with the simple exclusive OR algorithm, the RS algorithm provides the packet recovery capability upon burst packet loss.
  A-FEC helps to dynamically adjust the redundancy rate to reduce bandwidth waste and prevent continuous packet loss.

## Slide 43: FEC/A-FEC Implementation
FEC implementation process:
  A CPE at the transmit end receives and optimizes original packets. Meanwhile, it accumulates original packets and constructs a packet group.
  The CPE at the transmit end performs FEC encoding on the original packets in the group, and generates FEC redundancy packets.
  After receiving the original packets and redundancy packets, the CPE at the receive end detects the packet loss information, re-constructs a packet group, and recovers the lost packets.
  The CPE at the receive end performs FEC decoding on the received original packets and redundancy packets in the same group to obtain the original packets.
  The CPE at the receive end sends the original packets to the user.
4
3
2
1
CPE
CPE
VoIP data flow
P
4
3
2
1
P
4
3
2
1
Lost packet
FEC
A-FEC implementation process:
  The CPE at the receive end sends an FEC-ACK packet to the CPE at the transmit end. The packet contains real-time information about the packet loss rate and continuous packet loss on the network. The CPE at the transmit end adjusts the FEC redundancy rate according to the received FEC-ACK packet, alleviating or even eliminating the impact of packet loss on data transmission.

## Slide 44
(Multiple-answer question) Which of the following traffic steering policies are supported in Huawei SD-WAN Solution?
  Link quality–based traffic steering
  Bandwidth-based traffic steering
  Load balancing–based traffic steering
  Application priority–based traffic steering
(True or False) The scheduling following function is used to solve the problem of inconsistency between incoming and outgoing paths. The secondary party performs traffic routing, and the primary party follows the traffic steering result of the secondary party.
Notes: 1. ABCD
2. False

## Slide 45
Enterprises usually deploy multiple egress links to ensure network reliability. The SD-WAN intelligent traffic steering solution improves link utilization, properly utilizes each link, and preferentially ensures experience of high-value services.
A network device identifies the service type of traffic through FPI or SA, and applies the traffic steering policy matching the service type. Each service type has different link quality requirements. When the quality of a link cannot meet requirements, traffic is automatically switched to the secondary link.
Huawei SD-WAN Solution supports intelligent traffic steering based on the link quality, bandwidth, load balancing, and application priority. You can select a traffic steering policy based on actual situations. HQoS and WAN optimization can be deployed to improve user experience upon link congestion.