## Slide 1
V5R2
V1R1
Weijiongjian/wwx935519
2020.12.26
New
2019.01.25
2019.01.25
2019.01.25
2019.01.25
2019.01.25

## Slide 2: SD-WAN Security

## Slide 3
On a conventional enterprise WAN, enterprise branches connect to the headquarters, for example, through MPLS private lines, to access the headquarters or data center for service operations or Internet access. Security policies can be implemented at the headquarters, for example, deploying firewalls and other security devices, to manage and control branch-to-Internet access behaviors. The relatively closed network architecture of conventional enterprise WANs ensures security to some extent.
With the emergence of SD-WAN, the conventional closed architecture of enterprise WANs transforms to an open architecture, which enlarges the attack surface and brings new security challenges such as unauthorized access, data leakage, and network attacks.
This course describes how to cope with these security challenges to meet the confidentiality, integrity, availability, and traceability requirements of SD-WAN networks and provide a secure, reliable, and stable service running environment.

## Slide 4
On completion of this course, you will be able to:
  Describe the basic concepts and design principles of system security and service security in the SD-WAN Solution.
  Understand the security protocols and mechanisms used for communication between components of the SD-WAN Solution.
  Describe the basic principles and application scenarios of service security functions provided by the SD-WAN Solution.

## Slide 5
SD-WAN Security Overview
System Security
Service Security

## Slide 6: SD-WAN Security Risks
The SD-WAN Solution is built on a public network, and therefore its components are vulnerable to attacks and the communication between components faces security risks. In addition, user services carried by the SD-WAN Solution, such as site-to-site, site-to-Internet, and site-to-SaaS application access services, are threatened by various security risks. The SD-WAN Solution faces the following security challenges:
  Identity spoofing
  Data leakage
  Network attacks
  Service security requirements
RR
CPE
CPE
CPE
CPE
Branch
Branch
HQ/DC
Branch
SaaS applications
iMaster NCE-WAN
Internet
Notes: Identity spoofing: A component may be spoofed when it is registered and goes online. In this case, an identity authentication mechanism is required to ensure secure access of components and prevent identity spoofing.
Data leakage: Inter-component communication data and user service data are transmitted over a public network such as the Internet. Such data may be intercepted or tampered with, which affects system running.
Network attacks: Components provide interfaces for external interaction, and therefore are vulnerable to various attacks and intrusions such as flood attacks and application-layer attacks, which affect system availability.
Service security requirements: User services carried by the SD-WAN Solution have security requirements, such as filtering specific packets, blocking intrusion behaviors, and limiting access to URLs.

## Slide 7: SD-WAN Security Solution
To help enterprises better cope with the security challenges facing the SD-WAN Solution and take measures accordingly, Huawei defines security of the SD-WAN Solution from two aspects:
  System security: refers to the security of the SD-WAN Solution itself. Huawei SD-WAN Solution provides system security to ensure secure and reliable system running.
  Service security: refers to the security of services carried by the SD-WAN Solution. Huawei SD-WAN Solution provides security protection measures for enterprises to flexibly select based on their actual requirements to ensure secure and reliable running of user services.
RR
CPE
CPE
CPE
CPE
Branch
Branch
HQ/DC
Branch
SaaS applications
iMaster NCE-WAN
Internet
Security hardening
NETCONF
GRE over IPsec
BGP over GRE over IPsec
Notes: System security covers the following aspects:
  Inter-component communication security
  Component security
Service security covers the following aspects:
  Site-to-site access security
  Site-to-Internet access security
  Site-to-SaaS application access security
Huawei SD-WAN Solution provides the following service security functions:
  IPsec
  Firewall
  IPS
  URL filtering
  Advanced security VAS
  Third-party cloud security

## Slide 8
SD-WAN Security Overview
System Security
  Inter-Component Communication Security
  Component Security
Service Security

## Slide 9: Inter-Component Communication Security
Key components of the SD-WAN Solution include iMaster NCE-WAN, route reflectors (RRs), and customer-premises equipment (CPEs). The components use secure communication protocols to establish management, control, and data channels with each other to ensure communication security.
Management channel
  Management channels are established between CPEs or RRs and iMaster NCE-WAN.
  The management channel security mechanisms include identity authentication and secure data transmission.
Control channel
  Control channels are established between CPEs and RRs.
  The control channel security mechanisms include identity authentication and secure data transmission.
Data channel
  Data channels are established between CPEs.
  The data channel security mechanism ensures secure transmission of service data.
RR
CPE
CPE
Branch
HQ/DC
iMaster NCE-WAN
Management channel
Control channel
Internet/MPLS
Data channel

## Slide 10: Management Channel Security (1)
After a CPE is powered on and registers with iMaster NCE-WAN, iMaster NCE-WAN configures and delivers services to the CPE. In this process, the CPE and iMaster NCE-WAN may be spoofed because they reside on a public network.
Bidirectional certificate authentication is used to enable the CPE and iMaster NCE-WAN to verify the certificates of each other to ensure their validity.
Certificate Authority (CA): issues certificates.
CA certificate: refers to a certificate issued by a CA.
Device certificate: refers to a certificate issued by a CA to a device. Here, devices refer to the CPE and iMaster NCE-WAN.
Bidirectional certificate authentication
CPE
Send the CPE's certificates.
Send the certificates of iMaster NCE-WAN.
TCP
SSH (Callhome)
Verify the CPE's certificates.
Certificate validity
Certificate validity period
Verify the certificates of iMaster NCE-WAN.
Certificate validity
Certificate validity period
Bidirectional certification authentication succeeds.
Pre-configured device certificate and CA certificate
Pre-configured device certificate and CA certificate
iMaster NCE-WAN
Notes: iMaster NCE-WAN verifies the validity and validity period of a CPE's certificates.
A CPE verifies the validity and validity period of the certificates of iMaster NCE-WAN.
Callhome: proactive device registration function

## Slide 11: Management Channel Security (2)
Because CPEs and iMaster NCE-WAN reside on a public network, data transmitted between them may be leaked or tampered with.
The Network Configuration Protocol (NETCONF) provides a mechanism for managing network devices, which can be used to add, delete, modify, and obtain network device data. NETCONF uses the Secure Shell (SSH) protocol as the secure transport layer to provide a communication path for interaction between the client and server.
Secure Sockets Layer (SSL) is a security protocol that provides security and data integrity for network communication. It can be used to encrypt network connections between the transport layer and application layer.
Secure data transmission
CPE
The data security of management channels relies on the SSH and SSL protocols, with NETCONF over SSH, HTTP/2 over SSL, and file download over SSL implemented.
The encryption and verification functions provided by SSH and SSL ensure confidentiality and integrity of data during transmission.
NETCONF over SSH
File download over SSL
HTTP/2 over SSL
iMaster NCE-WAN
Notes: Management channels contain NETCONF connections, file download connections, as well as HTTP/2 connections for performance data reporting.
SSH provides secure remote login and other security network services over insecure networks.

## Slide 12: Control Channel Security
Because CPEs and RRs reside on a public network, control channels established between them may be spoofed. After control channels are established, data may be intercepted or tampered with during transmission in the channels.
RR
CPE
Send the CPE's certificates.
Send the RR's certificates.
DTLS
Verify the CPE's certificates.
Certificate validity
Certificate validity period
Verify the RR's certificates.
Certificate validity
Certificate validity period
Bidirectional certification authentication succeeds.
Pre-configured device certificate and CA certificate
Pre-configured device certificate and CA certificate
RR
CPE
The Datagram Transport Layer Security (DTLS) protocol provides a security solution for UDP transmission.
The data security of control channels relies on the DTLS and IPsec protocols, which ensure confidentiality and integrity of data during transmission.
BGP over GRE over IPsec
DTLS
Bidirectional certificate authentication
Secure data transmission
Notes: Control channels contain DTLS connections and BGP connections that are derived from DTLS connections. A CPE exchanges IPsec tunnel information with an RR through a DTLS connection and then establishes a BGP connection with the RR under the protection of the IPsec encryption mechanism.
The RR verifies the validity and validity period of the CPE's certificates.
The CPE verifies the validity and validity period of the RR's certificates.

## Slide 13: Data Channel Security
Inter-site data is transmitted across public networks, and may be leaked or tampered with during transmission. In this case, encryption is required to ensure security of data during transmission.
IPsec SA generation
RR
CPE-1
Secure data transmission
CPE
CPE
Data between CPEs is carried over the overlay tunnel established between them. IPsec is used to ensure confidentiality and integrity of the data during transmission.
GRE over IPsec
CPE-2
CPE-3
A Security Association (SA) defines elements for secure communication between two peers, such as security protocols as well as encryption and authentication algorithms.
CPEs establish IPsec SAs based on IPsec SA information advertised by RRs through control channels, but not through Internet Key Exchange (IKE) negotiation. This improves the establishment flexibility and scalability of IPsec tunnels.
IPsec SA information
SA
SA
SA
IPsec tunnel
IPsec tunnel
Notes: IPsec encryption can be enabled or disabled based on VPNs (departments).
The IKE protocol provides the mechanisms of automatic key negotiation and IPsec SA establishment to simplify IPsec configuration and maintenance.

## Slide 14
SD-WAN Security Overview
System Security
  Inter-Component Communication Security
  Component Security
Service Security

## Slide 15: Component Security (1)
Security of iMaster NCE-WAN
  iMaster NCE-WAN is a key component of the SD-WAN Solution, and its security directly determines the reliability and availability of the entire network. iMaster NCE-WAN must be deployed in a firewall-protected area and provide comprehensive security functions to mitigate security risks. The security functions include but are not limited to those in the following tables.
Category |  | Measures
Authentication and permission control | Identity authentication | Local and remote authentication (LDAP) Two-factor authentication (user name/password + SMS verification code)
 | Permission control | Role-based permission control Tenant- and domain-based permission control
Data protection | Key management | Secure encryption algorithms Hierarchical key management
 | Data storage | Data access control Encrypted data storage
 | Data transmission | Secure communication protocols Encrypted data transmission
Security detection and response | Attack detection | Attack detection from multiple dimensions, including ports, web pages, and operating systems
 | Intrusion prevention | Defense against various intrusion behaviors
 | Anti-DoS/DDoS | Defense against common traffic attacks
Category |  | Measures
Privacy protection |  | Strict access permission control
Security management | Security audit | Comprehensive logging and event recording functions
 | Secure upgrade and patch installation | Administrator authentication (Only authenticated administrators can perform upgrade and patch installation operations.)
System protection |  | Integrity protection and signature verification for software and patches
Security deployment |  | Zone planning, hierarchical deployment, and firewall deployment for isolation
Notes: The Lightweight Directory Access Protocol (LDAP) is used for accessing online directory services based on TCP/IP.

## Slide 16: Component Security (2)
Security of CPEs and RRs
  The security of the physical and network environments where CPEs and RRs reside must be ensured, so that the CPEs and RRs can run securely, reliably, and stably. The system architecture of CPEs and RRs complies with the three-layer and three-plane security isolation mechanism defined by ITU-T X.805, in which the management, control, and forwarding planes are isolated. This ensures that attacks on any of the planes do not affect other planes. In addition, CPEs and RRs themselves must have multiple security protection capabilities, including but not limited to those in the following table.
Category | Measures
Physical security | The service ports, serial ports, and services that are not in use are disabled to prevent attacks to devices through them.
Data security | Sensitive data, such as service data, user names, and passwords, are encrypted to prevent leakage. Data access permissions are controlled to prevent unauthorized access to data.
Authentication | Identity authentication and permission control are performed on user login behaviors. Local authentication and remote authentication (HWTACACS) are supported. User names and passwords are strictly protected, password complexity check is performed, and the anti-brute force cracking mechanism is implemented.
Attack defense | CPEs and RRs can defend against various network attacks, such as IP flood attacks, ICMP flood attacks, malformed packet attacks, and packet fragment attacks.
Security audit | A log system records all the system configuration operations and the exceptions that occur during running of the system, facilitating post-event auditing.
Notes: The ITU-T X.805 standard defines a security architecture for end-to-end communication systems. It defines three security layers (infrastructure, service, and application security layers) and three security planes (control, management, and forwarding planes). In addition, this security architecture protects each security plane at each security layer from eight security dimensions.
Huawei Terminal Access Controller Access Control System (HWTACACS) is an enhancement of TACACS (defined in RFC 1492), and is a centralized information exchange protocol using the client/server architecture. It uses TCP for transmission, and the TCP port number is 49.
The authentication, authorization, and accounting services provided by HWTACACS are independent of each other and can be implemented on different servers.

## Slide 17
SD-WAN Security Overview
System Security
Service Security
  Site-to-Site Access Security
  Site-to-Internet Access Security
  Site-to-SaaS Application Access Security

## Slide 18: Site-to-Site Access Security
  Service traffic between sites is transmitted over a public network (such as the Internet), and may be leaked or tampered with during transmission. In this case, IPsec is required to protect data. Site-to-site access security is also a type of data channel security.
CPE
CPE
CPE
CPE
Branch
Branch
HQ/
DC
Branch
SaaS applications
Site-to-site access traffic
Internet
MPLS
IPsec

## Slide 19: GRE over IPsec for Secure Data Transmission
Site-to-site access traffic is first encapsulated by GRE. GRE is simple. However, data is transmitted over GRE tunnels in clear text and prone to interception.
Typically, GRE is used together with IPsec on the live network. GRE is used to establish interconnection channels between sites, and IPsec is used to encrypt GRE tunnel packets.
GRE over IPsec data encapsulation
Encryption
Note: The IPsec transport mode is used as an example.
Branch
HQ
Encapsulate the header
GRE tunnel
S:IP1, D:IP2
Data
S:IP1, D:IP2
Data
GRE
S:IPA, D:IPB
GRE tunnel interface
GRE tunnel interface
IP1
IP2
IPA
IPB
S:IP1, D:IP2
Data
IPsec tunnel (external)
GRE tunnel (internal)
IPsec tunnel
ESP
Decapsulate the header

## Slide 20
SD-WAN Security Overview
System Security
Service Security
  Site-to-Site Access Security
  Site-to-Internet Access Security
  Site-to-SaaS Application Access Security

## Slide 21: Site-to-Internet Access Security
  Direct site-to-Internet access faces various security risks. In such access scenario, CPEs need to provide certain service security protection capabilities, such as firewall, intrusion prevention system (IPS), and URL filtering. In addition, Value-Added Service (VAS) functions can be deployed on SD-WAN networks to provide advanced security protection through physical firewalls deployed in off-path mode.
CPE
CPE
CPE
CPE
Branch
Branch
HQ/DC
Branch
SaaS applications
Access to the Internet
Access to SaaS applications
Internet
MPLS
Advanced security VAS
Firewall/IPS/URL filtering

## Slide 22: Basic Firewall Concepts: Zone
Security zones (or zones) are defined on a firewall. A security zone is a collection of networks connected through one or more interfaces. The firewall considers that data flows within a single security zone are trustful and no security policy is required. The firewall checks data and carries out security policies only when the data flows from one zone to another.
Zone | Default Security Priority
Untrust zone | 5 (low security level)
Demilitarized zone (DMZ) | 50 (medium security level)
Trust zone | 85 (high security level)
Local zone | A local zone is a device itself, including interfaces on the device. The local zone of a device is the highest-level security zone with a security priority of 100.
Trust zone
DMZ
Untrust zone
Interzone security policies
Internet
Egress (built-in firewall)
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: The names of default security zones on a firewall contain only lowercase letters and are case-sensitive. The security zones include:
  Untrust zone: defines insecure networks such as the Internet.
  DMZ: defines the zone where intranet servers reside. Intranet servers are frequently accessed by extranet devices but are not allowed to proactively access the extranet. Therefore, intranet servers face security risks, and need to be deployed in a security zone with a priority lower than the trust zone and higher than the untrust zone.
    A DMZ is originally a military term, referring to a partially controlled area between a military control area and a public area. A DMZ configured on a firewall is logically and physically separated from intranets and extranets.
    The servers such as WWW servers and FTP servers that provide network services for external devices are deployed in a DMZ. If these servers are deployed on an intranet, malicious users may exploit security vulnerabilities of some services to attack the intranet. If they are deployed on an extranet, their security cannot be ensured.
  Trust zone: defines the zone where intranet terminals reside.
  Local zone: defines a device itself, including the interfaces on the device. All packets constructed on and proactively sent from the device are considered to be sent from the local zone, and the packets to be responded and processed by the device (not only detected or forwarded) are considered to be received by the local zone. Local zone configurations cannot be modified. For example, interfaces cannot be added to the local zone.

## Slide 23
Notes:   Due to the particularity of the local zone, a security policy needs to be configured to permit packet exchange between the local zone and the security zone of a peer in scenarios where a device is required to send and receive packets.

## Slide 24: Basic Firewall Concepts: Interzone Direction
The traffic passing through a firewall is directional. An interzone security policy takes effect only when it is applied to the correct direction.
The direction of traffic on a firewall is determined by zone priorities.
  Inbound direction: refers to the direction of traffic flowing from a low-priority zone to a high-priority zone.
  Outbound direction: refers to the direction of traffic flowing from a high-priority zone to a low-priority zone.
Trust zone (priority: 85)
DMZ (priority: 50)
Untrust zone (priority: 5)
Internet
Egress (built-in firewall)
Outbound
Outbound
Inbound
Inbound
Firewall
IPS
URL Filtering
Advanced Security VAS

## Slide 25: Basic Firewall Concepts: Security Policy
Security policies can be used to control traffic between security zones on a firewall.
Trust zone
Untrust zone
Internet
Egress (built-in firewall)
Traffic A
Traffic B
Security policy | Trust -> Untrust (Outbound) |  | 
Policy 10 | Matching traffic A | Permit | IPS
Policy 20 | Matching traffic B | Deny | URL filtering
Default policy | Matching all traffic | Deny | 
Traffic A
Traffic C
A security policy must be applied to a direction.
The security policies are enforced in sequence. The traffic that does not match any security policy is denied based on the default policy.
When traffic matches a security policy, the firewall determines whether to permit the traffic or perform in-depth security protection based on the security policy.
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: A firewall basically protects a network from being attacked by any untrusted network while permitting legitimate communication between two networks. Security policies are used to check data flows passing through a firewall. Only the data flows that match the security policies with the action of Permit are allowed to pass through the firewall.
Security policies on a firewall can control the access permissions of intranet users to the extranet and control the access permissions between the subnets of different security levels on the intranet. In addition, security policies can control the access to a firewall itself, for example, restricting the IP addresses that can be used to log in to the firewall through Telnet and the web system and controlling communication between the NMS/NTP server and the firewall.
Security policies define rules for processing data flows on a firewall. The firewall processes data flows according to the rules. Therefore, the core functions of security policies are to filter the traffic passing through the firewall according to the defined rules and determine the next operation performed on the filtered traffic based on keywords.
Security policies on a firewall are a basic means for providing secure network access to the data flows passing through the firewall, and determine whether subsequent application data flows are processed. An NGFW analyzes traffic and retrieves traffic attributes, including the source security zone, destination security zone, source IP address, source region, destination IP address, destination region, user, service (source port number, destination port number, and protocol type), application, and time range.

## Slide 26: Application Scenarios of the Firewall Function
Branch
Local Internet access scenario
Centralized Internet access scenario
HQ
Branch
HQ
Internet access traffic of all branch sites is diverted to the HQ site and then to the Internet. The firewall function needs to be enabled on the CPE at the HQ site to isolate the intranet and extranet.
Overlay traffic
Underlay traffic
Internet access traffic of the branch site and HQ site is directly transmitted to the Internet from the local CPEs. The firewall function needs to be enabled on the CPEs at the branch site and HQ site to isolate the intranet and extranet.
CPE
CPE
CPE
CPE
Underlay traffic
Firewall
IPS
URL Filtering
Advanced Security VAS

## Slide 27: IPS Overview
The IPS is a network security mechanism.
It is used to detect intrusion behaviors (such as buffer overflow attacks, Trojan horses, and worms) by analyzing network traffic, and then block the intrusion behaviors in real time through certain response methods. The IPS helps to protect enterprise information systems and network architectures against intrusions.
The IPS has the following advantages:
  Real-time attack blocking
  In-depth protection
  All-round protection
  Internal and external prevention
  Constant update for up-to-date protection
Spyware
Trojan horses
Worms
Viruses
Campus network
Egress (built-in firewall, IPS function enabled)
Access switch
Authorized user
Authorized user
Authorized user
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: The IPS can detect and block network intrusions in real time. After detecting network intrusions, the IPS can automatically discard intrusion packets or block attack sources to fundamentally prevent attacks. The IPS has the following advantages:
  Real-time attack blocking: When the IPS deployed on a network in in-path mode detects network intrusions, it can block the intrusions and attack traffic in real time, minimizing impacts of the intrusions.
  In-depth protection: New attacks are hidden at the application layer of the TCP/IP protocol. The IPS can detect the content of application-layer packets, analyze and reassemble network data flows for protocol analysis and detection, and determine the traffic that must be blocked based on the attack type and policy.
  All-round protection: The IPS provides protection measures against a variety of attacks such as worms, viruses, Trojan horses, botnets, spyware, adware, Common Gateway Interface (CGI) attacks, cross-site scripting attacks, injection attacks, directory traversal attacks, information leaks, remote file inclusion attacks, overflow attacks, code execution, DoS attacks, and scanning attacks, comprehensively protecting network security.
  Internal and external protection: The IPS can protect enterprises from both external and internal attacks. The IPS can detect the traffic passing through and protect servers and clients.
  Constant update for up-to-date protection: The IPS signature database is constantly updated to maintain the highest security level. You can periodically update the IPS signature database from the update center to ensure effective intrusion prevention.

## Slide 28: Basic Concepts of IPS
The IPS needs to identify intrusion traffic before controlling the intrusion traffic. Intrusion traffic identification and control are implemented by the following functional modules:
  IPS signature database: defines features of various common intrusion behaviors and assigns a unique intrusion behavior ID for each kind of intrusion behavior feature.
  IPS signature: describes the features of an intrusion behavior on the network and the action to be taken for the intrusion behavior. IPS signatures can be pre-defined or user-defined.
  Signature filter: is a collection of signatures that meet specified filtering conditions. You can add multiple signatures to a signature filter and redefine the action to be taken for the traffic matching any signature in the signature filter.
  Exception signature: Some signatures in a signature filter can be configured with actions different from that of the signature filter.
  IPS profile: contains multiple signature filters and exception signatures. A CPE processes traffic based on an IPS profile.
Signature (feature + behavior)
A01 | Feature 1 Action: Alert
B01 | Feature 2 Action: Block
IPS profile
Signature filter 1
Protocol: HTTP
Action: Default
A01
Signature filter 2
Protocol: UDP
Action: Allow
B01
C01
C01 | Feature 3 Action: Block
Exception signature 1
Action: Allow
C01
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: By default, a CPE has multiple default IPS profiles for different application scenarios. The default IPS profiles can be viewed, copied, and referenced by security policies, but cannot be modified or deleted.
  strict: It contains all signatures and the action is block. It is applicable to all protocols and all threat categories. This profile applies to scenarios where all packets that match signatures need to be blocked.
  web_server: It contains all signatures and the default actions are used. It is applicable to the DNS, HTTP, and FTP protocols, and all threat categories. This profile applies to the scenarios where the CPE is deployed in front of a web server.
  file_server: It contains all signatures and the default actions are used. It is applicable to the DNS, SMB, NetBIOS, NFS, SunRPC, MSRPC, file transfer, and Telnet protocols, and all threat categories. This profile applies to the scenarios where the CPE is deployed in front of a file server.
  dns_server: It contains all signatures and the default actions are used. It is applicable to the DNS protocol and all threat categories. This profile applies to the scenarios where the CPE is deployed in front of a DNS server

## Slide 29
Notes:   mail_server: It contains all signatures and the default actions are used. It is applicable to the DNS, IMAP4, SMTP, and POP3 protocols, and all threat categories. This profile applies to the scenarios where the CPE is deployed in front of a mail server.
  inside_firewall: It contains all signatures and the default actions are used. It is applicable to all protocols and all threat categories. This profile applies to the scenarios where the CPE is deployed behind a firewall.
  dmz: It contains all signatures and the default actions are used. It is applicable to all protocols except NetBIOS, NFS, SMB, Telnet, and TFTP, and all threat categories. This profile applies to the scenarios where the CPE is deployed in front of a DMZ.
  outside_firewall: It contains all signatures and the default actions are used. It is applicable to all protocols and all threats except Scanner. This profile applies to the scenarios where the CPE is deployed in front of a firewall.
  ids: It contains all signatures and the action is alert. It is applicable to all protocols and all threat categories. This profile applies to the scenarios where the CPE is deployed in off-path mode as an IDS device.
  default: It contains all signatures and the default actions are used. It is applicable to all protocols and all threat categories. This profile applies to the scenarios where the CPE is deployed in in-path mode as an IPS device.

## Slide 30: IPS Implementation
When a data flow matches a security policy that contains an IPS profile, the CPE sends the data flow to the IPS module to match the signatures referenced by the IPS profile one by one.
If the data flow matches a signature, the action defined for the signature, such as block or alert, will be taken for the data flow.
IPS module
UDP video traffic
HTTP traffic
Egress (built-in firewall/IPS)
Internet
Signature (feature + behavior)
A01 | Type: Predefined Protocol: HTTP Action: Alert Others: condition A
B01 | Type: predefined Protocol: UDP Action: Block Others: condition B
IPS profile
Signature filter 1
Protocol: HTTP
Action: Default
A01
Signature filter 2
Protocol: UDP
Action: Default
B01
Actual action of the signature
A01 | Alert
B01 | Block
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: When a data flow matches multiple signatures, the actual action for the data flow is as follows:
  If the actions defined for all the matched signatures are alert, the action for the data flow is alert.
  If the action defined for any of the matched signatures is block, the action for the data flow is block.
When a data flow matches multiple signature filters, the action defined for the signature filter with the highest priority will be taken for the data flow.

## Slide 31: Application Scenarios of IPS
Branch
Local Internet access scenario
Centralized Internet access scenario
HQ
Branch
HQ
Internet access traffic of all branch sites is diverted to the HQ site and then to the Internet. The IPS function needs to be enabled on the CPE at the HQ site to block various intrusions from the Internet.
Internet access traffic of the branch site and HQ site is directly transmitted to the Internet from the local CPEs. The IPS function needs to be enabled on the CPEs at the HQ site and branch site to block various intrusions from the Internet.
CPE
CPE
CPE
CPE
IPS enabled
IPS enabled
IPS enabled
Overlay traffic
Underlay traffic
Underlay traffic
Firewall
IPS
URL Filtering
Advanced Security VAS

## Slide 32: Overview of URL Filtering
URLs, provided for manual operations on clients, open the first door for web attacks.
Uncontrolled access of employees to website resources severely reduces work efficiency, wastes network bandwidth resources of enterprises, and introduces threats such as viruses and Trojan horses from malicious sites to the intranet. In addition, a great deal of pornographic and violence information affects people's physical and psychological health.
URL filtering regulates users' online behaviors by controlling URLs accessible to users and permitting or denying users' access to some web resources.
Campus network
Egress (built-in firewall, URL filtering enabled)
Access switch
Authorized user
Authorized user
Authorized user
Pornographic and violent websites
Video and shopping websites
News websites
Denied web traffic
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: URL filtering regulates users' online behaviors by controlling their HTTP requests and permitting or denying users' access to certain network resources.

## Slide 33: URL Matching
Each web page on the Internet has a unique identifier, that is, the URL.
The URL format is as follows:
A regular expression is typically used for URL matching. The following table lists commonly used matching modes.
http://www.abcd.com:8080/news/education.aspx?name=tom&age=20
Path
Hostname
Query
:Port
Protocol
Matching Mode | Definition | Example | Matching Result
Prefix matching | All URLs that start with a specified character string are matched. | www.test.com* | All URLs that start with www.test.com are matched, for example, www.test.com/index.html.
Suffix matching | All URLs that end with a specified character string are matched. | *aspx | All URLs that end with aspx are matched, for example, www.test.com/news/solutions.aspx.
Keyword matching | All URLs that contain a specified character string are matched. | *sport* | All URLs that contain sport are matched, for example, sports.test.com/it/.
Exact matching | A URL is first matched against a specified character string. If the URL is not matched, the last directory in the URL is removed, and the remaining part is matched against the character string. If the URL is still not matched, the last directory is removed. This process continues until the URL matches the character string. | www.example.com | Based on matching rules, the following URLs match www.example.com: www.example.com www.example.com/news www.example.com/news/en/
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: Each web page on the Internet has a unique identifier, that is, the URL.
URLs fully describe the addresses of web pages or other resources on the Internet. To put it simply, a URL is a web address.
The URL format is protocol://hostname[:port]/path[? query]
  protocol: Used application protocol. HTTP is the most commonly used protocol. You do not need to enter http:// when the protocol is HTTP.
  hostname: DNS host name or IP address of the web server.
  port: (Optional) Communication port. Each transmission protocol has a default port number.
  path: Directory or file address on the web server.
  query: (Optional) This field is used to transmit parameters to dynamic web pages.

## Slide 34: Implementation of URL Filtering
When an HTTP request matches a URL, a CPE functioning as a gateway processes the HTTP request according to the URL filtering mode and URL filtering process. The following URL filtering modes are supported:
  Blacklist- or whitelist-based URL filtering: A CPE filters received HTTP requests based on the URL whitelist or blacklist configured on it.
  Category-based URL filtering: After receiving an HTTP request, a CPE queries the URL category in the predefined URL category database. After the URL category is queried, the CPE processes the HTTP request according to the action defined for the URL category.
Internet
Egress (built-in firewall, URL filtering enabled)
www.huawei.com
www.game.com
URL filtering |  | 
Whitelist | *huawei* | Permit
Blacklist | *game* | Deny
Visit www.huawei.com.
Visit www.game.com.
Firewall
IPS
URL Filtering
Advanced Security VAS
Notes: On a gateway, URL filtering is implemented as follows:
  After the gateway receives an HTTP GET or POST request from a user, it checks the validity of the request based on the configured policies.
    If the URL is valid, the HTTP request is permitted and the user can browse the website.
    If the URL is invalid, the gateway pushes an alarm page and blocks the HTTP connection.
URL categories fall into user-defined and predefined URL categories.
  User-defined categories are configured and maintained by administrators. Administrators can perform more refined control over URLs in user-defined categories than over URLs in predefined categories.
  Predefined categories contain common URLs in the system. Unlike user-defined categories, predefined categories enable administrators to easily control accessible and inaccessible URL categories.

## Slide 35: Application Scenarios of URL Filtering
Application scenarios of URL filtering
Randomly visiting various websites at branch sites may bring security risks. URL filtering regulates users' online behaviors by controlling URLs accessible to users and permitting or denying users' access to some web resources.
URL filtering applies to the following scenarios:
  Site-to-legacy site access
  Site-to-SD-WAN site access
  Site-to-Internet access
Branch
Branch
CPE
CPE
URL filtering enabled
HQ
CPE
1
2
3
Traffic for accessing an SD-WAN site
Traffic for accessing the Internet
Traffic for accessing a legacy site
Overlay traffic
Underlay traffic
Firewall
IPS
URL Filtering
Advanced Security VAS

## Slide 36: Application Scenarios of Advanced Security VAS
Application scenarios
A physical firewall is deployed in off-path mode and provides advanced security protection for centralized Internet access traffic of sites.
After the VAS function is deployed, the centralized Internet access traffic of sites is diverted to the LAN-side physical firewall connected to the CPE at the HQ site in off-path mode. After being processed by the firewall, the traffic is transmitted to the Internet through the underlay network.
Branch
Branch
CPE
CPE
Physical firewall deployed in off-path mode
HQ
CPE
Firewall
Firewall
IPS
URL Filtering
Advanced Security VAS

## Slide 37
SD-WAN Security Overview
System Security
Service Security
  Site-to-Site Access Security
  Site-to-Internet Access Security
  Site-to-SaaS Application Access Security

## Slide 38: Site-to-SaaS Application Access Security
  As traditional enterprise applications are gradually migrated to the cloud, branch sites of enterprises access applications on the cloud through the Internet, which may face security risks. In such service scenarios, a third-party cloud security gateway can be deployed to implement security protection on the cloud.
CPE
CPE
CPE
CPE
Branch
Branch
HQ/DC
Branch
SaaS applications
Access to SaaS applications
Internet
MPLS
Third-party cloud security gateway

## Slide 39: Application Scenarios of Third-Party Cloud Security
Application scenarios
As traditional enterprise applications are gradually migrated to the cloud, branch sites of enterprises can directly access applications on public clouds through the Internet, which faces security risks. In such service scenarios, security protection can be implemented on the cloud.
The SD-WAN Solution supports interconnection with a third-party cloud security gateway, so that traffic for accessing SaaS applications on the cloud can be sent to the third-party cloud security gateway for security protection.
CPE
CPE
Branch
Branch
SaaS applications
Third-party cloud security gateway
Access control
Threat detection
Attack defense
Data protection
...
iMaster NCE-WAN

## Slide 40: Deployment Modes of Third-Party Cloud Security Gateways
Deployment modes
CPE
Branch
Access point 2
GRE
GRE
Access point 1
CPE1
Branch
Access point 1
Access point 2
GRE
CPE2
GRE
GRE
To improve network reliability, a third-party cloud security gateway usually provides two access points to establish GRE tunnels with a CPE.
Single-gateway scenario
  A CPE establishes one active GRE tunnel and one standby GRE tunnel with the two access points of the third-party cloud security gateway.
Dual-gateway scenario
  Two CPEs establish four GRE tunnels (two pairs of active and standby GRE tunnels) with the two access points of the third-party cloud security gateway.
Single-gateway scenario
Dual-gateway scenario
Notes: Policy-based routing (PBR) is configured on CPEs to divert the traffic for accessing SaaS applications to GRE tunnels. In addition, CPEs can use network quality analysis (NQA) to detect network reachability and perform an active/standby tunnel switchover.

## Slide 41
(Multiple-answer question) Which of the following are included in the inter-component communication security of the SD-WAN Solution?
  Management channel security
  Data channel security
  Control channel security
  Connection channel security
(True or False) The built-in firewall function enables CPEs to control the traffic between different security zones. For example, when the priorities of zone 1 and zone 2 are 20 and 60 respectively on a firewall, the traffic from zone 1 to zone 2 is outbound traffic.
Notes: ABC
False

## Slide 42
SD-WAN security includes system security and service security.
System security includes the security of components (iMaster NCE-WAN, CPEs, and RRs) as well as the security of management, control, and data channels established between the components.
Service security includes the site-to-site, site-to-Internet, and site-to-SaaS application access security. The firewall, IPS, URL filtering, advanced security VAS, and third-party cloud security functions can effectively defend against various security threats.