## Slide 1
Course Code
Product
X.X
V1R1
Hou Jianqiang/00405872
2019.12.27
He Junjian/WX580230
Update
Author/ID
Reviewer/ID
Type
Author/ID
Reviewer/ID
Type
Author/ID
Reviewer/ID
Type
Author/ID
Reviewer/ID
Type
Author/ID
Reviewer/ID
Type

## Slide 2: SD-WAN Intelligent O&M

## Slide 3
When maintaining an SD-WAN network, network engineers need to quickly locate and rectify faults. In traditional CLI-based O&M mode, however, global traffic paths cannot be detected, and fault locating and rectification are time-consuming and inefficient and require high skills for network engineers. Therefore, CLI-based O&M is not applicable to quickly deployed large-scale networks.
iMaster NCE-WAN provides visualized monitoring on network topologies and services, helping O&M personnel learn about the network running status and adjust the network accordingly. It also offers the alarm function to facilitate fault locating and rectification and the log function to facilitate fault source tracing.
This course describes the monitoring, alarm, and log functions provided by iMaster NCE-WAN for intelligent O&M from the perspective of tenants.
Notes: This course is based on Huawei SD-WAN Solution.

## Slide 4
On completion of this course, you will be able to:
  Describe visualized monitoring functions provided by iMaster NCE-WAN.
  Describe fault diagnosis methods provided by iMaster NCE-WAN.

## Slide 5
Overview of Intelligent O&M
Monitoring
Maintenance

## Slide 6: Overall Intelligent O&M Architecture of the SD-WAN Solution
Northbound APIs
iMaster NCE-WAN
Southbound APIs
System Portal
MSP Portal
Tenant Portal
Development API
Zero touch provisioning (ZTP)
Email-based deployment
USB-based deployment
DHCP-based deployment
Monitoring
Overlay topology
Alarm
Site monitoring
Inter-site monitoring
Device monitoring
Link monitoring
Application monitoring
Maintenance
Ping & Traceroute
AQM
Remote SSH
Diagnosis information collection
Patch upgrade
Device replacement
NETCONF
RPC & Notification
Telemetry
HTTP/2
Syslog
HTTPS
File transfer
SSH
Devices
ZTP
Email-based deployment
USB-based deployment
DHCP-based deployment
Monitoring (data collection)
Log
Alarm
Interface or tunnel traffic statistics collection
Tunnel quality detection
Application identification
NetStream
TCP FPM
Maintenance
SSH
IP FPM
Device resource usage
Patch upgrade
Diagnosis file
Log server
Notes: The main APIs between O&M components include:
  NETCONF:
    iMaster NCE-WAN delivers service configurations to devices through NETCONF.
    Devices send alarms to iMaster NCE-WAN through NETCONF notification.
    iMaster NCE-WAN uses NETCONF RPC messages to remotely maintain devices.
  Telemetry:
    Telemetry is used to encrypt HTTP/2 connections between devices and iMaster NCE-WAN.
    Devices use Telemetry to periodically send collected performance data to iMaster NCE-WAN for performance monitoring.
    Historical trend analysis provides high-precision monitoring data sources.
  Syslog:
    Devices can send logs to a third-party log server using the Syslog protocol.
  HTTPS:
    Devices and iMaster NCE-WAN use HTTPS for download and management of files such as software packages and patches.
  SSH:
    iMaster NCE-WAN allows O&M personnel to remotely log in to devices through SSH for O&M and diagnosis.

## Slide 7
Overview of Intelligent O&M
Monitoring
Maintenance

## Slide 8: Monitoring Overview
Monitoring is the basis of visualized O&M. iMaster NCE-WAN can monitor network and service status and statistics, providing basis for subsequent fault diagnosis, fault analysis, and policy application.
iMaster NCE-WAN provides multi-dimensional monitoring capabilities, including the dashboard, site monitoring, service (link and application) monitoring, and alarm monitoring. The monitoring data can be sorted, searched, and filtered by date.

## Slide 9: Customizing Information Displayed on the Dashboard
Information displayed on the dashboard, such as alarm information, site health status, top worst links, and task information, can be customized based on customer requirements.

## Slide 10: Overlay Topology Monitoring
With the topology monitoring function, O&M administrators can view the overlay network status and check whether the overlay deployment result is correct.
On the overlay topology, O&M administrators can also check the quality of inter-site links through link quality measurement (LQM) and discover inter-site link problems in advance.
M and I indicate different routing domains.

## Slide 11: Customizing AQM and LQM
O&M administrators can customize the AQM and LQM calculation rules and modify the thresholds of factors in the calculation formulas.
  Take AQM as an example. Choose Monitoring > Monitor Configuration > AQM from the main menu.
  Click Modify to adjust the weights of the delay and packet loss rate in the AQM calculation formula.
  Drag the slider to adjust the delay and packet loss rate threshold ranges for Excellent, Good, Average, and Poor.
Slider

## Slide 12: Site Monitoring (1)
Choose Monitoring > Monitoring > Site from the main menu.
Click a site to view more information.

## Slide 13: Site Monitoring (2)
Overview
  View basic information about a site.
  View the topology of a site.
  View IP resources of a site.
  View statistics on a site's visitor quantity, average AQM, bandwidth utilization, and throughput.
Device
  Monitor information about a single device, such as the CPU usage, memory usage, hard disk usage, and temperature.
Link
  Monitor links of a single site.
Application
  Monitor applications of a single site.

## Slide 14: Inter-Site Monitoring
Choose Monitoring > Monitoring > Inter-Site from the main menu.
View the worst 5 inter-site links by LQM.
View the top 5 inter-site links by traffic.

## Slide 15: Application Monitoring
O&M administrators can view statistics on the communication quality and visits of network-wide applications.
Choose Monitoring > Monitoring > Application from the main menu.
View AQM distribution information about network-wide applications and worst 5 applications by AQM.

## Slide 16
Overview of Intelligent O&M
Monitoring
Maintenance

## Slide 17: Overview of Maintenance Tools
iMaster NCE-WAN provides the following maintenance tools:
  Alarm
  Diagnosis
  Log
  Maintenance
  Device maintenance
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis
Notes: When iMaster NCE-WAN itself, devices, services, or systems managed by it, or its connections with peripheral systems are faulty or have potential risks, alarms are generated. With the alarm management function, O&M administrators can view alarm information in real time and troubleshoot faults based on alarm details and handling suggestions in a timely manner, ensuring normal running of services.
On iMaster NCE-WAN, O&M administrators can set device alarm thresholds, for example, CPU and memory usage alarm thresholds. When a threshold is reached, an alarm is reported to iMaster NCE-WAN.
When iMaster NCE-WAN is running, it can record system management operation logs and run logs, which facilitate audit and fault locating.

## Slide 18: Alarm Classification
Alarm Category | Description | Administrator
Controller alarm | Alarms generated by iMaster NCE-WAN, including: Alarms about services managed by iMaster NCE-WAN, such as topology change alarms Alarms generated upon exceptions of iMaster NCE-WAN, such as license, cluster, or system status exceptions Alarms generated due to disconnections between iMaster NCE-WAN and peripheral systems | System administrator
Device alarm | Alarms and events reported by devices to iMaster NCE-WAN, for example, device restart, user logout, interface protocol change, and smart policy change | Tenant administrator
Alarm Category | Description
Current alarm | Include uncleared and unacknowledged alarms, acknowledged and uncleared alarms, and unacknowledged and cleared alarms.
Historical alarm | Include alarms that have been cleared and acknowledged.
Masked alarm | Alarms that do not need to be handled can be masked. Masked alarms are displayed in the masked alarm list. If such alarms are generated later, they will not be displayed in the current alarm list.
Event | Events are alarms of the lowest severity and indicate that certain events happen. Events do not need to be handled.
Classification by alarm source
Classification by alarm status
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 19: Alarm Severities and Status
Status Name | Alarm Status | Description
Acknowledgment status | Acknowledged and unacknowledged | The initial acknowledgment status is Unacknowledged. A user who views an unacknowledged alarm and plans to handle it can acknowledge the alarm. When an alarm is acknowledged, its status changes to Acknowledged. Acknowledged alarms can be unacknowledged. When an alarm is unacknowledged, its status is restored to Unacknowledged. O&M administrators can also configure auto acknowledgment rules to automatically acknowledge alarms.
Clearance status | Cleared and uncleared | The initial clearance status is Uncleared. When the fault that causes an alarm is rectified, a clearance notification is automatically reported to the alarm management system and the clearance status changes to Cleared. For some alarms, clearance notifications cannot be automatically reported to the alarm management system. O&M administrators need to manually clear these alarms after corresponding faults are rectified. The background color of cleared alarms is green.
Alarm Severity | Color | Description | Handling Policy
Critical |  | Services are affected. Corrective measures must be taken immediately. | Rectify the fault immediately. Otherwise, services may be interrupted or the system may break down.
Major |  | Services are affected. If the fault is not rectified in a timely manner, serious consequences may occur. | Rectify the fault in a timely manner. Otherwise, key services will be affected.
Minor |  | The fault affects services slightly currently, but needs to be rectified to avoid more severe faults. | Find out the cause of the alarm and rectify the fault.
Warning |  | A potential or imminent fault that affects services is detected, but services are not affected currently. | Handle warning alarms based on the network and NE running status.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 20: Alarm and Event Types
Alarm or Event Type | Description
Communications alarm | Alarms caused by failures of the communications in an NE, between NEs, between an NE and a management system, or between management systems, for example, device communication interruption alarms.
Service quality alarm | Alarms caused by service quality deterioration, for example, device congestion alarms.
Equipment alarm | Alarms caused by physical resource faults, for example, card fault alarms.
Operation alarm | Alarms generated when the required services cannot run properly due to problems such as service unavailability, faults, or incorrect invocation, for example, alarms caused by service rejection, service exit, and procedural errors.
Security alarm | Alarms generated when security issues are detected by a security service or mechanism, for example, alarms caused by authentication failures, confidential disclosure, and unauthorized access.
Object creation | Events generated when a managed object (MO) instance is created.
Object deletion | Events generated when an MO instance is deleted.
Relationship change | Events generated when relationship attributes of an MO change.
State change | Events generated when status attributes of an MO change.
Route change | Events generated when routes change.
File transfer status | Alarms or events reported when file transfer succeeds or fails.
… | …
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 21: Internal Alarm Handling Process
After alarms are reported to the alarm management system, the system processes the alarms, including masking alarms, performing correlation analysis, and redefining severities.
Start
Name redefinition
Automatic acknowledgment
Alarm masking
Intermittent or toggling (pre-processing)
Alarm update
Severity and type redefinition
Correlation analysis
Alarm pre-processing
Archiving alarms to the database
Intermittent or toggling (post-processing)
Alarm post-processing
Real-time notification
End
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 22: Description of the Internal Alarm Handling Process
Operation | Description
Name redefinition | After receiving alarms, the alarm management system matches the alarms against the name redefinition rule and changes the names of the alarms that meet the name redefinition rule.
Alarm masking | The alarm management system discards the alarms that meet the masking rules, that is, the alarms are not archived to the database, or records the alarms in the masked alarm data table.
Intermittent or toggling (pre-processing) | The alarm management system records the alarms that meet the intermittent or toggling handling rules in the intermittent or toggling data table.
Alarm update | The alarm management system updates the information of current alarms, such as clearing alarms and changing the severities, based on the reported alarm changes.
Severity and type redefinition | The alarm management system redefines the alarms that meet the severity and type redefinition rules.
Correlation analysis | The alarm management system marks the alarms that meet the correlation rules as root alarms or correlative alarms, and handles the root alarms or correlative alarms based on the actions in the rules.
Automatic acknowledgment | The alarm management system automatically acknowledges the alarms that meet the auto acknowledgment rules. The alarms that are automatically acknowledged are recorded in the historical alarm data table.
Archiving alarms to the database | The alarm management system archives the remaining alarms to the database. Post-processing is not performed on the alarms that are masked or moved to historical alarms during alarm pre-processing. The information on the alarms is updated in real time.
Intermittent or toggling (post-processing) | The alarm management system analyzes the alarms in the intermittent or toggling data table and handles the alarms that meet the intermittent or toggling policies.
Alarm merging | The alarm management system merges the alarms that meet the merging conditions.
Real-time notification | The alarm management system updates the alarm information on the alarm interface in real time.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 23: Alarm Management on iMaster NCE-WAN
Click to acknowledge an alarm.
Click to clear an alarm.
Click to set a masking rule.
Click Export to export the list of alarms that meet the current filter criteria to a CSV file.
Click Filter to set alarm filter criteria.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 24: Customizing Alarm Items on iMaster NCE-WAN
Alarm items, such as the alarm ID and clearance time, can be customized on iMaster NCE-WAN.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 25: Setting Alarm Masking Rules on iMaster NCE-WAN
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 26: Alarm Settings on iMaster NCE-WAN
Choose Maintenance > Alarm > Alarm Settings from the main menu. Alarm colors, display modes, and sounds can be set.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 27: Configuring Alarm Notification on iMaster NCE-WAN
Choose Maintenance > Alarm > Alarm Notification from the main menu. Enable Mail notification and set related parameters, so that alarm notifications will be sent to the specified recipient by email.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 28: Viewing Configuration Results
Choose Maintenance > Provisioning Result > Site Configuration Status from the main menu. Click the Configuration Result tab and select a site to view the site's configuration result.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 29: Diagnosis Overview
iMaster NCE-WAN provides the following diagnosis functions:
Ping
  On iMaster NCE-WAN, an administrator delivers a ping command to a CPE to check the connectivity, packet loss rate, and average delay of the underlay and overlay networks between the CPE and the destination host.
Trace
  On iMaster NCE-WAN, an administrator delivers a traceroute command to a CPE to track the route packets take from the CPE to the destination host. iMaster NCE-WAN then provides the visualized diagnosis result for the administrator.
Application quality diagnosis
  An administrator delivers a command for checking the quality of a specified application to a CPE. The CPE then uses IP FPM technology to check the quality of the specified application (only the packet loss rate can be checked).
Fault information collection
  If a CPE or network fault occurs but the root cause cannot be located using the preceding methods, O&M administrators can collect the CPE's diagnosis information with one click and send the information to Huawei technical support for fault locating.
HQ
Branch site
Branch site
Legacy MPLS
site
Public cloud site
Internet
MPLS
POP/
Backbone network
CPE
CPE
CPE
IWG
vCPE
Gateway
Gateway
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 30: Diagnosis: Ping and Trace
Choose Maintenance > Diagnosis > Ping from the main menu.
On the Ping page that is displayed, configure parameters for checking the network connectivity, including the source site, device, network type, link or virtual private network, source IP address, destination IP address/URL, packet size, and number of packets.
Click Start to start the network connectivity check.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis
Notes: The trace operation is similar to the ping operation.

## Slide 31: Diagnosis: AQM
Choose Maintenance > Diagnosis > Application Quality Monitor from the main menu. On the Application Quality Monitor page that is displayed, click Create to create an application traffic detection task.
Set the task name, source site, and destination site, select the application to be diagnosed from the application list, and click . Then, click OK. The task starts automatically.
To diagnose an application again, select the target diagnosis task and click Start to start diagnosis. After sufficient data is collected, click Stop.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 32: Diagnosis: Fault Information Collection
Choose Maintenance > Diagnosis > Fault Collection from the main menu. The Fault Collection page is displayed.
Two methods are available for downloading fault diagnosis logs from iMaster NCE-WAN.
  To export fault diagnosis logs of all devices in a collection task, click in the Operation column of the task.
  To export fault diagnosis logs of a single device, click next to the device to display the fault information collection details. Then click in the Operation column to export fault diagnosis logs.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 33: Log Management Overview
When iMaster NCE-WAN is running, it can record system management operation logs and run logs, which facilitate audit and fault locating.
Tenant administrators can configure devices to report device logs to a third-party log server and view device logs on the log server, facilitating device management and maintenance.
A tenant administrator configures log server parameters on a CPE through iMaster NCE-WAN.
Logs generated by the CPE are reported through the syslog channel.
The log server receives and displays log information.
The tenant administrator queries the device logs saved on the log server.
The tenant administrator queries logs on the iMaster NCE-WAN web UI.
MPLS
Internet
CPE1
CPE2
Log server
1
Configure an IP address for the log server.
2
Report logs.
3
Process logs.
4
Query logs.
5
Query logs on the controller.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis
Notes: When iMaster NCE-WAN is running, it can record system management operation logs and run logs, which facilitate audit and fault locating.

## Slide 34: Log Types
Log Type | Description
Operation logs | Record all add, delete, and modify operations triggered by users or iMaster NCE-WAN to facilitate audit.
Security logs | Record operations related to user accounts, such as login to and logout of iMaster NCE-WAN as well as password change, to facilitate audit.
Device login and logout logs | Record device login and logout information to facilitate audit.
Device logs | Because the storage space of iMaster NCE-WAN is limited, device logs are not saved. Therefore, tenant administrators cannot view and audit historical logs of devices. To resolve this problem, they need to configure a third-party log server to which devices report logs, and then can log in to the log server to view the logs for device management and maintenance.
Log Type | Description
Operation logs | Record all add, delete, and modify operations triggered by users or iMaster NCE-WAN to facilitate audit.
Security logs | Record operations related to user accounts, such as login to and logout of iMaster NCE-WAN as well as password change, to facilitate audit.
Run logs | Record status information generated during the running of iMaster NCE-WAN and execution of tasks. Run logs can be used to diagnose iMaster NCE-WAN faults.
Tenant administrator
System administrator
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 35: Log: Operation Logs
On the Log page, O&M administrators can manage security logs, operation logs, device login and logout logs, and device system logs.
Operation logs
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 36: Device Maintenance
iMaster NCE-WAN provides the device upgrade, device certificate management, SA upgrade, and device configuration backup functions on the Maintenance > Device Maintenance page.
iMaster NCE-WAN also provides multiple device management functions, such as remote device login, indicator blinking, and one-click device restart.
SA upgrade
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 37: Device Maintenance: Remote Login to a Device
Choose Design > Site Agile Design > Devices Management from the main menu.
Click the name of a device to access the device details page.
Click Command Line in the upper right corner to remotely log in to the device's CLI. Select the device administrator authentication mode.
Obtain the device's routing table and ARP table with the device entry query function provided by iMaster NCE-WAN.
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 38: Device Maintenance: Web Management System
Alarm
Configuration Result
Log
Device Maintenance
Diagnosis

## Slide 39
(Single-answer question) Which protocol does iMaster NCE-WAN use to deliver service configurations to devices?
  NETCONF
  Telemetry
  Syslog
  SSH
(Multi-answer question) Which of the following device information can be viewed on the iMaster NCE-WAN web UI?
  CPU usage
  Memory usage
  Hard disk usage
  Temperature
Notes: 1. A
2. ABCD

## Slide 40
iMaster NCE-WAN provides multi-dimensional monitoring capabilities, including the dashboard, site monitoring, service (link and application) monitoring, and alarm monitoring. The monitoring data can be sorted, searched, and filtered by date.
iMaster NCE-WAN provides various O&M tools, such as alarm management, diagnosis, log management, and device maintenance. With the alarm management function, users can learn about alarm information in real time, and rectify faults based on alarm details and handling suggestions to ensure normal service running. They can perform ping and trace operations to check network connectivity, and view operation logs, security logs, as well as device login and logout logs. In addition, they can upgrade the SA signature database or software versions of devices based on actual requirements, and log in to CPEs through SSH.
These O&M tools are used together to implement intelligent O&M.