## Slide 1
Wu Yue/wwx291773
2020-05-30
New

## Slide 2: GRE Technology

## Slide 3
A large enterprise has a large number of branches. To enable branches to communicate with each other or with the headquarters, the private line or VPN technology needs to be used.
The private line is expensive but has excellent performance; the VPN is cheaper than the private line but performance is lower.
Generic Routing Encapsulation (GRE) is the most commonly used VPN technology on the live network. With GRE, an enterprise can build an intranet for the branches and headquarters at a very low cost.
This section describes the basic concepts and fundamentals of GRE.

## Slide 4
Upon completion of this course, you will be able to:
  Describe basic concepts of tunnels.
  Describe fundamentals of GRE.
  Describe basic security mechanisms of GRE.
  Describe application scenarios of GRE.
  Complete basic GRE configuration.

## Slide 5
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
GRE Configuration

## Slide 6: GRE Background
With the development of enterprises, more and more enterprises need to communicate between branches and headquarters. Private lines (such as MPLS and SDH/MSTP private lines) need to be leased for communication between the headquarters and branches. However, private lines are expensive. For small- and medium-sized enterprises or cross-border companies, the cost is high.
With the development of the Internet, the Internet has sufficient bandwidth and coverage. Therefore, it is more feasible to implement communication on the intranet between the headquarters and branches through the Internet. GRE is proposed in this background.
Through GRE tunnels, the enterprise network can be established between the branch and headquarters based on the Internet.
Internet
Branch site
Branch site
HQ
Branch site
Interconnection between branches and HQ
Internet
GRE tunnel
GRE tunnel
GRE tunnel

## Slide 7: Introduction to Tunneling Technologies
GRE is one of tunneling technologies. A tunnel is similar to a bridge. Forwarding channels are established on the underlying network (for example, Internet). Users can establish a tunnel network by themselves without the intervention of the underlying network provider (for example, an ISP).
There are many tunneling technologies, such as MPLS, GRE, Layer 2 Tunneling Protocol (L2TP), and Virtual Extensible LAN (VXLAN). The following figure shows the implementation of tunnel data forwarding.
Branch
HQ
Internet
Inner Header
Data
Outer Header
Inner Header
Data
Inner Header
Data
Encapsulate the outer header
Inner Header
Data
Outer Header
The device forwards the packet on the underlying network based on the outer header. The underlying network is unaware of the inner data.
Decapsulate the outer header
Inner Header
Data
Inner Header
Data
Tunnel
Implementation of tunnel data forwarding
Tunnel data forwarding

## Slide 8: Basic Concepts of GRE
As a Layer 3 tunneling technology, GRE encapsulates packets of a protocol into packets of another protocol to transparently transmit packets over GRE tunnels. This technology enables packet transmission between the HQ and branches.
GRE tunnels can transmit IPv4/IPv6 unicast, multicast, and broadcast packets.
GRE packet format:
L2 Header | New IP Header | GRE Header | Raw IP Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
32 bits
Notes: Description of fields in a GRE header:
Field | Description
C | Checksum verification bit. The value 1 indicates that the Checksum field is inserted into the GRE header. The value 0 indicates that the GRE header does not contain the checksum field.
K | Key bit. The value 1 indicates that the Key field is inserted into the GRE header. The value 0 indicates that the GRE header does not contain the keyword field.
Recursion | Number of layers where GRE packets are encapsulated. The value of this field is increased by 1 after one GRE encapsulation is complete. If the number of encapsulation layers is greater than 3, the packet is discarded. This field is used to prevent packets from being encapsulated continuously.
Flags | Reserved field. The value must be 0.
Version | Version. The value must be 0.
Protocol Type | Type of the passenger protocol. A common passenger protocol is the IPv4 protocol, with the value of 0800. The protocol number of Ethernet over GRE is 0x6558.
Checksum | Checksum of the GRE header and the payload.
Key | Key used to authenticate the packet at the receive end.

## Slide 9: GRE Fundamentals
The GRE tunnel is a Layer 3 tunnel and mainly carries IPv4/IPv6 packets. GRE encapsulates the outer IP header so that data can be transmitted on the public network. In this way, enterprise branches and the headquarters can communicate with each other.
The following figure shows the process of forwarding packets over a GRE tunnel.
Branch
HQ
Encapsulate the outer header
The device forwards the packet on the underlying network based on the outer IP header.
Decapsulate the outer header
GRE tunnel
S: IP1, D: IP2
Data
S: IP1, D: IP2
Data
GRE
S: IPA, D: IPB
GRE tunnel interface
GRE tunnel interface
IP1
IP2
IPA
IPB
S:IP1，D:IP2
Data
GRE
S: IPA, D: IPB
S: IP1, D: IP2
Data

## Slide 10: Keepalive Detection
The current GRE protocol does not have the link status detection function. If the remote interface is unreachable, the GRE tunnel cannot be terminated immediately. As a result, the source continuously forwards packets to the peer. The peer, however, cannot receive packets because the tunnel is unreachable. In this case, traffic is interrupted.
The keepalive detection function monitors tunnel status to check whether the remote end is reachable.
Keepalive timeout interval = Sending interval (5s by default) x Retry count (3 by default)
GRE tunnel
GRE Keepalive
Timeout timer
GRE Keepalive
Reply with a keepalive message within the timeout interval.
The keepalive message does not expire and the tunnel status is normal.
Notes: Keepalive detection functions as follows:
  After being enabled on the source end of a GRE tunnel, the source end starts a timer to periodically send and count keepalive messages. The number of sent keepalive messages increases by one each time a keepalive message is sent.
  The destination end sends a response message to the source end each time it receives a keepalive message from the source end.
  If the source end receives a reply packet before the counter value reaches the preset value, it considers the remote end reachable. If the source end does not receive any response message before the counter reaches the preset value, specifically, the retry count, the source end considers the peer end unreachable and resets the counter. Then, the source end terminates the tunnel connection. In this case, the source interface still sends Keepalive messages to the remote interface. When the remote interface becomes Up, the source interface becomes Up and sets up a tunnel with the remote interface.

## Slide 11
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
GRE Configuration

## Slide 12: Security Threats to GRE Tunnels
GRE tunnels are used to transmit data between branches and the HQ. Data is not encrypted and may be tampered with.
There are potential risks in GRE tunnel establishment. Attackers can forge IP addresses to establish GRE tunnels between authorized and unauthorized devices.
GRE data tampering
GRE tunnel
Data tampering
Unauthorized GRE tunnel setup
GRE tunnel
Unauthorized GRE tunnel
GRE
Outer Header
Payload
GRE
Outer Header
Payload

## Slide 13: GRE Data Check and Verification
Checksum verification is an end-to-end check on encapsulated packets.
If the C bit in the GRE header is set to 1, the checksum is valid. The sender calculates the checksum based on the GRE header and payload. Then it sends out the packet that carries the checksum. After receiving the packet, the receiver also calculates the checksum and compares the result with the checksum carried in the packet. If they are the same, the receiver further processes the packet. Otherwise, it discards the packet.
Outer Header | GRE Header | Inner Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
Data verification used to prevent data tampering
GRE tunnel
Payload
Data tampering
GRE
Payload
GRE
Outer Header
C=1,Checksum=A
C=1,Checksum=B
Verification fails and data is discarded.
Inconsistent checksum
Outer Header
Notes: You can enable or disable checksum verification on both ends of a tunnel in actual applications. If checksum verification is enabled on the local end and disabled on the remote end, the local end does not check checksum values of received packets, but checks checksum values of packets to be sent. If checksum verification is disabled on the local end and enabled on the remote end, the local end checks checksum values of received packets, but does not check checksum values of packets to be sent.

## Slide 14: GRE Key
Key authentication is used to verify validity of a tunnel interface. This security mechanism prevents tunnel interfaces on two devices at both ends of a GRE tunnel from incorrectly identifying and receiving packets from other devices.
If the K bit in the GRE header is set to 1, a four-byte Key field is inserted into the GRE header. Both the receiver and the sender need to authenticate the key.
GRE tunnel
Unauthorized GRE tunnel
GRE Key=10
GRE Key=10
GRE Key=20
The tunnel cannot be established because the keys are inconsistent.
The GRE key is used to prevent unauthorized GRE tunnel establishment.
Outer Header | GRE Header | Inner Header | Payload
C | 0 | K | 0 | 0 | Recursion | Flags | Version | Protocol Type
Checksum (Option) |  |  |  |  |  |  |  | 0
Key (Option) |  |  |  |  |  |  |  | 
Notes: This field identifies traffic in a tunnel. Packets of the same traffic use the same key. During packet decapsulation, GRE identifies data packets of the same traffic based on the key. Packets will pass verification only when the two ends of the tunnel use the same Key field. If packets fail the verification, they will be discarded. Successful authentication requires that both ends are either configured with the same Key field or not configured with the Key field.

## Slide 15
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
GRE Configuration

## Slide 16: Using GRE to Build an Intranet Between the HQ and Branches
GRE tunnels can transmit IPv4/IPv6 unicast, multicast, and broadcast packets. Dynamic routing neighbor relationships can be configured between branches and the HQ through GRE tunnels, facilitating intranet interconnection between branches and the HQ.
GRE tunnel
Branch 1
HQ
Branch 2
GRE tunnel
OSPF area 1
OSPF area 2
OSPF area 0

## Slide 17: GRE Over IPsec
GRE is simple. However, data is transmitted over a GRE tunnel in cleartext and can be easily obtained. On the live network, GRE is usually used together with IPsec. The GRE technology is used to establish the internal network connection between the branch and headquarters, and the IPsec technology is used to encrypt GRE tunnel packets.
GRE over IPsec data encapsulation
Internet
IPsec tunnel
IPsec tunnel
GRE tunnel
IP data
IPsec data
IP data

## Slide 18
GRE Fundamentals
GRE Security Mechanisms
GRE Application Scenarios
GRE Configuration

## Slide 19: Basic GRE Configuration
Context:
  A small- or medium-sized enterprise has the headquarters (hub) and a branch (Spoke1) that are located in different areas. The enterprise requires that the hub and Spoke1 can communicate with each other.
Configuration roadmap:
  Ensure that the public network interfaces of the spoke and hub can communicate with each other.
  Configure a GRE tunnel between the hub and spoke.
Branch
HQ
GRE tunnel
Spoke1
Hub

## Slide 20: Creating a GRE Tunnel Between the Spoke and Hub
The configuration on the spoke is similar to that on the hub. The configuration commands are as follows.
Branch
HQ
GRE tunnel
Spoke
Hub
System-view
interface tunnel <interface-num> //Create a tunnel interface.
ip address <ip-address> //Set the IP address of the tunnel interface. This IP address is used as the next hop of the route for intranet communication.
tunnel-protocol gre //Set the tunnel type to GRE.
source <ip-address> //Set the source address of the tunnel, which is the same as the source IP address in the outer IP header of GRE-encapsulated packets.
destination <ip-address> //Set the destination address of the tunnel, which is the same as the destination IP address in the outer IP header of GRE-encapsulated packets.
gre key <key-num> //(Optional) Configure a GRE key that is used to check whether a GRE tunnel can be established.
The GRE tunnel needs to be configured on the devices at both ends of the tunnel.
The configuration roadmap is as follows:
  Ensure that the public network interfaces of the spoke and hub can communicate with each other.
  Create GRE tunnels on the spokes and hub.
  Configure the source and destination addresses of the GRE tunnel.

## Slide 21: Diverting Traffic to a GRE Tunnel
There are many methods to divert traffic to a GRE tunnel, such as OSPF, static routes, and BGP.
For details about how to configure static or dynamic routes, see the product documentation of Huawei.
Branch
HQ
GRE tunnel
Spoke1
Hub
Configure static or dynamic routes.
Configure static or dynamic routes.

## Slide 22: Checking the GRE Configuration
After the configuration is complete, run the following commands to check the configuration.
System-view
display interface tunnel [interface-number] //Check the working status of the tunnel interface.
display tunnel-info tunnel-id [tunnel-id] //Check tunnel information.

## Slide 23
(Multiple-answer question) How do we ensure GRE tunnel security?
  IPsec
  GRE data verification
  GRE key
  SSL
Notes: 1. ABC

## Slide 24
GRE tunnels make it easy and cost-effective to establish intranet communication between enterprise branches and the HQ.
GRE adds an outer IP header to IPv4/IPv6 data packets and builds a GRE tunnel, so that an ISP is not involved in data forwarding on the intranet.
GRE tunnel security relies on the following technologies:
  IPsec is used to encrypt GRE tunnel data.
  GRE data verification is used to ensure that data in the GRE tunnel is not tampered with.
  The GRE key is used to control setup of a GRE tunnel between sites.