## Slide 1
Wu Yue/wwx291773
2020.05.30
New

## Slide 2: HA Technologies

## Slide 3
In addition to network connectivity, network reliability is also an important indicator for measuring network quality.
The guidelines for improving network reliability are to detect and correct faults in a timely manner.
Various technologies, including bidirectional forwarding detection (BFD), network quality analyzer (NQA), and IP flow performance measurement (FPM), are available to detect faults in a timely manner.
There are many technologies for correcting faults in a timely manner, such as Virtual Router Redundancy Protocol (VRRP), fast reroute (FRR), non-stop forwarding (NSF), and smart policy routing (SPR).
Different technologies vary according to different application scenarios.
This course introduces some commonly used high reliability (HA) technologies at the link, network, and service levels.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the common technologies and fundamentals of link detection.
  Describe the common technologies and fundamentals of link backup.
  Understand the fundamentals and application scenarios of VRRP.
  Understand the fundamentals and application scenarios of Smart Application Control (SAC).
  Understand the fundamentals and application scenarios of SPR.

## Slide 5
Link Reliability
  Link Detection
  Link Backup
Network Reliability
Service Reliability

## Slide 6: Overview of Link Detection
Fluctuation of network link quality affects service quality. How to quickly detect link quality is the first step in improving link quality.
There are many protocols and technologies for detecting link quality, which are classified into two types:
  Link connectivity detection technologies:
    BFD
    Ethernet in the First Mile (EFM)
    Connectivity Fault Management (CFM)
  Link quality detection technologies:
    NQA
    IP FPM
BFD, EFM, and CFM are used to detect network link connectivity.
NQA and IP FPM are used to detect network quality.
BFD, EFM, CFM
NQA, IP FPM
On the live network, BFD is typically used to detect link connectivity, and NQA is typically used to detect link quality.

## Slide 7: Overview of BFD
BFD provides a universal, standardized, media-independent, and protocol-independent fast failure detection mechanism. It has the following advantages:
  Provides low-overhead and fast failure detection for channels between adjacent forwarding engines.
  Performs uniform detection for all media and protocol layers in real time.
BFD is a simple Hello protocol. Two systems establish a BFD session channel and periodically send BFD packets to each other. If one system does not receive BFD packets from the other system within a certain period, the system considers that a fault occurs on the channel.
Application layer
Transport layer
Network layer
Data link layer
Physical layer
Application layer
Transport layer
Network layer
Data link layer
Physical layer
BFD session detection
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: Only one BFD session can be established in a data path. If different applications need to use different BFD parameters on the same data path, use the BFD parameters that can meet the requirements of all applications to configure a unique BFD session and enable the status changes of the BFD session to be reported to all the applications.

## Slide 8: BFD Detection
Two systems establish a BFD session and periodically send BFD control packets along the path between them. If one system does not receive BFD control packets within a certain period, the system considers the path faulty. BFD has two modes: asynchronous mode and demand mode.
Asynchronous mode
In asynchronous mode, two systems periodically send BFD control packets to each other. If one system does not receive any BFD control packet from the other system within the detection period, it declares the session down.
Demand mode
To verify connectivity, one system sends a BFD control packet to the other system. If it receives a response packet from the other system within the detection period, the BFD session between the two systems remains up. Otherwise, it declares the session down.
R1
R2
BFD session
...
R1
R2
BFD session
BFD packet
BFD packet
BFD packet
BFD packet
BFD packet
BFD packet
Sends BFD control packets periodically
Sends BFD control packets on demand
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: The essential difference between the asynchronous mode and demand mode is that the detection location is different. In asynchronous mode, the local end sends BFD control packets at a certain interval, the detection location is on the remote end, and the remote end checks whether the local end periodically sends BFD control packets. In demand mode, the local end checks whether the BFD control packets sent by itself are responded.

## Slide 9: BFD Echo
The BFD echo function enables the local system to send BFD echo packets to the remote system, which then forwards the echo packets back along the same path in order to perform detection. This function provides rapid failure detection.
The BFD echo function is classified into passive BFD echo and one-arm BFD echo based on application scenarios.
Passive BFD echo
Passive BFD echo applies only to single-hop IP link scenarios and must work with asynchronous BFD. In asynchronous echo mode, slow detection is performed in asynchronous mode and fast detection is performed in echo mode at the same time. This function applies when the BFD detection capabilities of the two ends are inconsistent.
One-arm BFD echo
One-arm echo applies only to single-hop IP link scenarios. A one-arm BFD echo session can be established on a device that supports BFD. After receiving a one-arm BFD echo session packet, devices that do not support BFD immediately loop back the packet, implementing fast link failure detection. This function is typically used when one system does not support BFD.
R1
R2
BFD-capable device
BFD-incapable device
Initiates an echo request packet
1
Directly loops back the packet at the network layer
2
Determines whether the link is operational
3
R1
R2
Echo initiator
Echo Passive
Echo responder
BFD control packet detection
BFD echo packet detection
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: The process of establishing a passive BFD echo session is as follows:
  R2 functions as a BFD session initiator and sends an asynchronous BFD packet to R1. The Required Min Echo RX Interval field carried in the packet is a nonzero value, requiring R1 to support BFD echo.
  After receiving the packet, R1 finds that the value of the Required Min Echo RX Interval field in the packet is a nonzero value. If R1 has passive BFD echo enabled, it checks whether any ACL that restricts passive BFD echo is referenced. If such an ACL is referenced, only the BFD sessions that match specific ACL rules can enter the asynchronous echo mode. If no ACL is referenced, BFD sessions immediately enter the asynchronous echo mode.
  R2 periodically sends BFD echo packets, and R1 sends BFD echo packets (with the source and destination IP addresses being the local IP address, and the destination physical address being R2's physical address) at the locally configured minimum interval for receiving BFD packets. Both R1 and R2 start a receive timer, with the receive interval being the same as the interval at which they each send BFD packets.
  After R1 and R2 receive BFD echo packets from each other, they immediately loop back the packets at the forwarding layer. R1 and R2 also send asynchronous BFD packets to each other at an interval much smaller than that for sending echo packets.

## Slide 10
Notes: The one-arm echo function does not require both ends to negotiate the echo capability. That is, it applies when only one end supports BFD. The local device that has one-arm BFD echo enabled sends a special BFD packet (both the source and destination IP addresses in the IP header are the local IP address, the destination physical address is the physical address of the peer device, and the MD and YD in the BFD payload are the same). After receiving the packet, the peer device immediately loops the packet back to the local device to determine link reachability. One-arm BFD echo can be used on low-end devices that do not support BFD.

## Slide 11: BFD Association
BFD association involves the monitoring module, track module, and application module.
Monitoring module
BFD
module
Track module
Application module
VRRP
Static routing
Policy-based routing (PBR)
Interface backup
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: The monitoring module monitors the link status and network performance and notifies the track module of the detection result.
After receiving the detection result from the monitoring module, the track module changes the track status in a timely manner and notifies the application module of the change.
The application module takes actions according to the track status, implementing association with the monitoring module and track module.

## Slide 12: BFD Configuration
Configure BFD.
system-view
bfd //Enable BFD globally.
bfd [session-name] bind peer-ip [ip-address] //Create a BFD session and specify the peer device with which the BFD session needs to be established.
discriminator local [discr-value] //Set the local discriminator of the BFD session. The value must be the same as the value of discriminator remote on the peer device.
discriminator remote [discr-value] //Set the remote discriminator of the BFD session. The value must be the same as the value of discriminator local on the peer device.
commit //Commit the configuration.
BFD detection
BFD detection
system-view
ip route-static [ip-address] [mask-length] [next-hop] track bfd-session [session-name] //Associate the BFD session with a static route.
The configuration roadmap is as follows:
  Enable BFD on devices at both ends.
  Specify the IP addresses of devices at both ends to establish a BFD session.
  Configure matching local and remote discriminators on both ends to determine the BFD session.
  Commit the configuration and start the BFD session.
  Associate the BFD session with protocols as required. BFD sessions can be associated with a variety of protocols.
Associate BFD with static routes.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: For more configuration commands, see Huawei product manuals.

## Slide 13: Verifying the BFD Configuration
After BFD is configured, check information about the configured BFD session.
system-view
display bfd interface [ interface] //Check information about the BFD-enabled interface.
display bfd session all verbose //Check BFD session information.
display bfd statistics //Check global BFD statistics.
display bfd statistics session all //Check BFD session statistics.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 14: Overview of NQA
To visualize the quality of network services and allow users to check whether the quality of network services meets requirements, the following measures must be taken:
  Enable devices to provide network service quality information.
  Deploy probe devices to monitor network service quality.
The preceding measures require devices to provide statistical parameters such as the delay, jitter, and packet loss rate and require dedicated probe devices. These requirements increase investments on devices.
When NQA is deployed on devices, dedicated probe devices do not need to be deployed, effectively reducing costs. NQA can accurately test the network running status and output statistics.
It measures network performance and collects statistics about the response time, jitter, and packet loss rate in real time.
TCP delay detection
DNS delay detection
Total HTTP delay detection
NQA test
NQA client
NQA server
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: Additionally, NQA measures the performance of different protocols running on the network. This facilitates real-time collection of network performance counters, such as the total HTTP connection delay, TCP connection delay, DNS resolution delay, file transfer rate, FTP connection delay, and DNS resolution error rate.

## Slide 15: NQA Fundamentals
NQA sends datagrams of a specific service to test the quality of the service on the live network.
In an NQA test, devices on both ends are NQA client and NQA server, which are also called the source and destination. The NQA client initiates an NQA test. Test instances can be configured for the NQA client through the CLI or web system. NQA then places the test instances into test queues for scheduling.
An NQA test can be associated with other modules. That is, NQA notifies other modules of the test result, and other modules take actions according to the test result.
TCP delay detection
DNS delay detection
Total HTTP delay detection
NQA test instance
NQA client
NQA server
NQA test
Data
Adds a timestamp to NQA test data
NQA test
Data
The NQA server returns a packet after receiving the data
NQA test
Data
Compares the timestamp with the local time to determine the test result
NQA test result
Other modules
The NQA test result can be used by other modules
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: NQA can be associated with VRRP, static routing, interface backup, Internet Group Management Protocol (IGMP) proxy, IP address pool, domain name system (DNS) server, and PBR.
The maximum delay, maximum packet loss rate, and maximum jitter can be configured for an NQA test instance. If the delay, jitter, or packet loss rate tested in an NQA test instance exceeds the configured values, the NQA test instance fails.

## Slide 16: NQA Association
NQA association involves the monitoring module, track module, and application module.
Monitoring module
NQA
module
Track module
Application module
VRRP
Static routing
PBR
Interface backup
IGMP proxy
IP address pool
DNS server
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: The monitoring module monitors the link status and network performance and notifies the track module of the detection result.
After receiving the detection result from the monitoring module, the track module changes the track status in a timely manner and notifies the application module of the change.
The application module takes actions according to the track status, implementing association with the monitoring module and track module.

## Slide 17: NQA Test Types
NQA can be used to test the network quality of commonly used services:
Application-layer tests
DHCP test
DNS test
FTP test
HTTP test
Transport-layer tests
TCP test
UDP test
UDP jitter test
SNMP test
Connectivity test
ICMP test
ICMP jitter test
LSP ping test
LSP trace test
Trace test
VPLS ping test
VPLS trace test
VPLS PW ping test
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 18: NQA Server Configuration (TCP Test)
Run the following commands on the NQA TCP test server:
Many NQA test types are available. The following example configures a TCP delay test.
A server can be configured for a TCP test. In some tests, such as an HTTP test, a real HTTP server is typically used as the server.
The configuration roadmap is as follows:
  Configure the IP address and TCP port to be checked in the NQA TCP test.
system-view
nqa-server tcpconnect [ip-address] [port-num] //Configure the IP address and TCP port to be checked in the NQA TCP test.
TCP delay detection
NQA test
NQA client
NQA server
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: The NQA server needs to be configured for some tests, including:
  TCP test
  UDP test
  UDP jitter test
Other NQA tests require a real server. For example, an HTTP test requires an NQA test request to be sent to the web server.

## Slide 19: NQA Client Configuration (TCP Test)
Run the following commands on the NQA TCP test client:
TCP delay detection
NQA test
NQA client
NQA server
Many NQA test types are available. The following example configures a TCP delay test.
The configuration roadmap is as follows:
  Create an NQA test instance.
  Set the test instance type.
  Configure the server IP address.
  Configure test parameters, such as the maximum delay and test period.
system-view
nqa test-instance [admin-name] [test-name] //Specify the administrator name and name of the NQA test instance.
test-type [type] //Set the test type. If TCP services need to be tested, set the test type to TCP.
destination-address ipv4 [ip-address] //Configure the destination IP address for the test.
destination-port [port-num] //(Optional) Set the destination port for the test.
timeout [time] //(Optional) Set the maximum delay.
start now //Start the test immediately.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 20: Verifying the NQA Configuration
After an NQA test instance is configured, run the following commands to check the configuration of the test instance.
On the client:
On the server:
system-view
display nqa application //Check the NQA test instance type for the service.
display nqa-parameter //Check the parameter settings of the current test instance.
display nqa support-server-type //Check the server types supported by NQA.
display nqa support-test-type //Check the test types supported by NQA.
display nqa-agent //Check the NQA client status and configuration.
system-view
display nqa-server //Check NQA server information.
display nqa-server session //Check NQA client information on the NQA server.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 21: Overview of IP FPM
With the advent of the cloud computing era, end-to-end service performance measurement becomes essential. However, the commonly used NQA technology has the following defects in end-to-end network performance measurement scenarios:
  NQA simulates service packet forwarding on the network by constructing service packets. Therefore, the collected performance statistics are not accurate.
  NQA does not support end-to-end performance measurement across network layers, and cannot monitor or measure network performance in a multipath scenario of IP networks.
IP flow performance measurement (IP FPM) can effectively solve these problems. It is a general IP network performance measurement solution. IP FPM can directly measure service packets, and the measurement data can reflect the performance of IP networks. In addition, IP FPM can monitor the changes of services carried by IP networks online and accurately reflect the running status of services.
IP FPM test point
IP FPM test point
IP Header
Data
IP Header
Data
Test the actual traffic.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 22: IP FPM Fundamentals
Traffic entering a network from a border device will leave the network from another border device. To determine end-to-end service performance, you only need to measure the specific traffic on these ingress and egress border devices.
IP FPM sets the ToS or Flags field in the IP header of a packet to color the packet, helping ingress and egress devices measure the packet loss rate or jitter of specific traffic.
DCP
DCP
MCP
TLP
TLP
Data
IP Header
Data
IP Header
IP FPM colors data packets.
NMS/controller
The DCP sends the statistics collected by the TLP to the MCP.
The TLP calculates the number of colored packets.
The TLP calculates the number of colored packets.
The DCP sends the statistics collected by the TLP to the MCP.
The MCP summarizes the statistics and calculates the packet loss rate and delay.
(Optional) The MCP reports results to the NMS or controller.
1
2
2
3
3
4
5
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Notes: TLP is short for target logical port.
  TLPs are interfaces on the edge nodes of the network and provide the following functions:
  Collect statistics about the packet loss rate and delay.
  Generate statistics, such as the number of packets sent and received, traffic bandwidth, and timestamp.
  An In-Point-TLP collects statistics about service flows it receives. An Out-Point-TLP collects statistics about service flows it sends.
DCP is short for Data Collecting Point.
  DCPs are edge nodes on the network and provide the following functions:
  Manage and control TLPs.
  Collect the statistics generated by TLPs.
  Report the statistics to an MCP.
MCP is short for Measurement Control Point.
  MCPs are intermediate nodes on the network and provide the following functions:
  Collect the statistics reported by DCPs.
  Summarize and calculate the statistics.
  Report the statistics to user terminals or the network management system (NMS).

## Slide 23: IP FPM Measurement Mechanism
IP FPM supports packet loss measurement and delay measurement.
Packet loss measurement: The number of colored packets entering the network (PI) and the number of colored packets leaving the network (PE) are measured within a certain period. The packet loss rate is calculated based on the PI and PE using the following formula: Lost Packet = PI - PE.
Delay measurement: A device records the time when data is sent and received and calculates the delay based on the time difference between the time when data is sent and the time when data is received on different devices: Two-way delay = Delay of the forward traffic + Delay of the return traffic.
Colored data
Measures the number of colored packets within a measurement period.
PI
PE
Measures the number of colored packets within a measurement period.
DCP
DCP
DCP
DCP
Sends the colored data and records the time T1.
Receives the colored data and records the time T2.
Sends the colored data and records the time T3.
Forward direction
Return direction
2D = (T2 - T1) + (T4 - T3)
Introduction to BFD
Introduction to NQA
Introduction to IP FPM
Receives the colored data and records the time T4.

## Slide 24: Configuring an MCP
DCP
DCP
MCP
TLP
TLP
Two roles, MCP and DCP, need to be configured for IP FPM.
The configuration roadmap is as follows:
  Enable MCP globally.
  Configure an MCP ID.
  Configure an IP FPM test instance.
  Configure a DCP ID.
system-view
nqa ipfpm mcp //Enable MCP globally.
mcp id [id] //Configure an MCP ID. It is an IP address used for communication between the MCP and DCPs. Ensure that the MCP and DCP are reachable to each other through their IP addresses.
authentication-mode hmac-sha256 key-id [id] cipher [password] //(Optional) Configure authentication for IP FPM protocol packets.
instance [id] //Configure an IP FPM instance. The instance ID must be unique in the MCP management domain.
dcp [id] //Configure a DCP ID. It is an IP address used for communication between an MCP and a DCP. Ensure that the MCP and DCP are reachable to each other at the IP layer.
Configure an MCP.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 25: Configuring a DCP
Two roles, MCP and DCP, need to be configured for IP FPM.
The configuration roadmap is as follows:
  Enable DCP globally.
  Configure a DCP ID.
  Configure an MCP ID.
  Configure an IP FPM test instance.
  Configure a target flow to be monitored.
  Configure a TLP.
system-view
nqa ipfpm dcp //Enable DCP globally.
dcp id [id] //Configure a DCP ID. It is an IP address used for communication between an MCP and a DCP. Ensure that the MCP and DCP are reachable to each other at the IP layer.
authentication-mode hmac-sha256 key-id [id] cipher [password] //(Optional) Configure authentication for IP FPM protocol packets.
mcp [id] //Configure an MCP ID. It is an IP address used for communication between an MCP and a DCP. Ensure that the MCP and DCP are reachable to each other at the IP layer.
instance [id] //Configure an IP FPM instance.
flow forward protocol [TCP | DCP] source [ip-address/port] destination [ip-address | port] //Configure the target flow to be monitored.
tlp [tlp-id] [in-point ingress | out-point egress] //Configure a TLP ID to determine whether the TLP is an inbound or outbound interface.
loss-measure enable continual //Configure packet loss measurement.
delay-measure enable two-way tlp [tlp-id] continual //Configuration delay measurement.
interface [interface-type interface-name] //Enter the interface view.
ipfpm tlp [tlp-id] //Bind the TLP ID to the interface.
DCP
DCP
MCP
TLP
TLP
Configure a DCP.
Introduction to BFD
Introduction to NQA
Introduction to IP FPM

## Slide 26: Verifying the IP FPM Configuration
IP FPM commands display IP FPM performance statistics, helping monitor the IP FPM running status.
system-view
display ipfpm statistic-type [loss | twoway-delay ] instance [instance-id] //Check the performance statistics of a specified IP FPM instance.

## Slide 27
(Multiple-answer question) Which of the following services can be checked by NQA?
  DNS
  HTTP
  IGMP
  ICMP
Notes: 1. ABD

## Slide 28
BFD is mainly used to check the connectivity of the network layer. BFD can be associated with static routes, dynamic routes, and interface backup to facilitate fast network convergence.
NQA can detect network connectivity and network quality based on services, for example, NQA can measure the TCP delay, DNS delay, and TCP jitter. NQA can be associated with static routes, dynamic routes, and interface backup to speed up network convergence.
NQA simulates services for detection, so the test result is not accurate. IP FPM is mainly used to improve the detection accuracy. IP FPM colors packets and measures the colored packets on network border devices to check the actual service quality.

## Slide 29
Link Reliability
  Link Detection
  Link Backup
Network Reliability
Service Reliability

## Slide 30: Link Backup
To ensure reliability, a network egress is typically connected to multiple WAN links in active/standby mode. When one link is faulty (for example, an interface is faulty, the link is faulty, or the link bandwidth is insufficient), services can be immediately switched to another link. To meet this requirement, the following technologies are often used on the live network:
  Interface backup
  IP floating route
Internet
MPLS
IP routing-table
Net1 IF1 primary link
Net1 IF2 backup link
Interface backup
IP floating route
IF1
IF2
Primary link
Net1

## Slide 31: Interface Backup
Interface backup refers to the backup between specific interfaces on the same device. When an interface is faulty or the bandwidth is insufficient, traffic can be fast switched to a standby interface. The standby interface then transmits services or load balances network traffic.
Interface backup operates in either active/standby or load balancing mode.
  Interface backup in active/standby mode: One interface is the active interface, and the others are standby interfaces. When the active interface fails or the network quality is poor, a standby interface transmits data.
  Interface backup in load balancing mode: One interface is the active interface, and the others are standby interfaces. When the bandwidth of the active interface is insufficient, a standby interface is enabled. Then both the active and standby interfaces transmit data.
Interface Backup
IP Floating Route

## Slide 32: Interface Backup in Active/Standby Mode
In active/standby mode, only a single interface transmits services at any time. The mechanism of interface backup in active/standby mode is as follows:
  When the active interface IF1 is working properly, interfaces IF2 and IF3 are in the standby state.
  When IF1 is faulty or the link quality does not meet requirements, IF2 with the highest priority enters the forwarding state.
  After IF1 recovers, traffic is switched back to IF1.
Interface backup in active/standby mode can detect only faults on direct links but not the remote link status or overall link quality. In this case, interface backup in active/standby mode can be associated with NQA, BFD, or routing tables.
IF1 (active)
IF2 (standby, priority 10)
IF3 (standby, priority 5)
NQA
BFD
Route detection
Interface Backup
IP Floating Route

## Slide 33: Interface Backup in Load Balancing Mode
In load balancing mode, if the bandwidth of the active interface on a device is insufficient, the device uses standby interfaces to transmit data.
  When traffic on the active interface IF1 does not reach the upper bandwidth limit, IF1 alone forwards the traffic.
  When the traffic reaches the upper bandwidth limit, the standby interface IF2 with the highest priority is enabled to forward traffic at the same time.
  If one standby interface cannot meet service bandwidth requirements, the standby interface IF3 with the second highest priority is used. The rest can be deduced by analogy until the standby interface that meets service bandwidth requirements is used.
  When the traffic volume decreases, standby interfaces are shut down in ascending order of priority.
IF1 (active)
IF2 (standby, priority 10)
IF3 (standby, priority 5)
Interface Backup
IP Floating Route
Notes: Interface backup in load balancing mode is implemented only based on interface bandwidth usage and cannot be associated with BFD or NQA.

## Slide 34: Configuring Interface Backup
IF1 (active)
IF2 (standby, priority 10)
The configuration roadmap is as follows:
  Ensure the network connectivity of the primary and backup links.
  Configure standby interfaces and their priorities.
system-view
interface [interface-type interface-num] //Enter the active interface view.
standby interface [interface-type interface-num] [Priority] //Configure a standby interface for the active interface. If multiple standby interfaces are required, you need to run this command multiple times.
standby time delay [enable-delay] [disable-delay] //Configure the interface switching delay. enable-delay specifies the delay in a switchover from the active interface to the standby interface. disable-delay specifies the delay in a switchback from the standby interface to the active interface.
Configure interface backup:
Interface Backup
IP Floating Route

## Slide 35: Configuring Interface Backup Association
Associate interface backup with NQA:
IF1 (active)
IF2 (standby, priority 10)
Interface backup can be associated with NQA, BFD, and routing tables to improve service transmission reliability.
The configuration roadmap is as follows:
  Enable the association function when configuring a standby interface on the active interface.
system-view
interface [interface-type interface-num] //Enter the standby interface view.
standby track nqa [admin-name] [test-name] //Associate interface backup with NQA.
system-view
interface [interface-type interface-num] //Enter the standby interface view.
standby track bfd-session session-name [name] //Associate interface backup with BFD.
Associate interface backup with BFD:
Associate interface backup with routing tables:
system-view
interface [interface-type interface-num] //Enter the standby interface view.
standby track ip route [ip-address] [mask-length] //Associate interface backup with routing tables.
Interface Backup
IP Floating Route

## Slide 36: Configuring Interface Backup in Load Balancing Mode
Configure interface backup in load balancing mode:
IF1 (active)
IF2 (standby, priority 10)
Interface backup in load balancing mode enables multiple interfaces to transmit data at the same time.
The configuration roadmap is as follows:
  Configure standby interfaces on the active interface.
  Set the percentage threshold for load balancing.
system-view
interface [interface-type interface-num] //Enter the active interface view.
standby interface [interface-type interface-num] [Priority] //Configure a standby interface for the active interface. If multiple standby interfaces are required, you need to run this command multiple times.
standby threshold [enable-threshold] [disable-threshold] //Configure the percentage threshold for load balancing. enable-threshold specifies the threshold for enabling a standby interface, and disable-threshold indicates the threshold for disabling the standby interface.
Interface Backup
IP Floating Route

## Slide 37: IP Floating Route
An IP floating route is a static route. It provides a backup route when the primary route fails. A floating route is installed in the IP routing table only when the next hop of the primary route is unreachable.
The IP floating route is implemented based on the Pre value in the IP routing table. In most cases, the Pre value of the backup route is set to be greater than that of the primary route.
The active/standby switchover of IP floating routes is typically performed based on the interface status. Therefore, to detect the status of the entire path, NQA or BFD on the live network is often associated with IP floating routes. If NQA or BFD sessions fail, the primary route is considered ineffective.
IF1
IF2
IF3
NQA
BFD
IP routing-table
Net1 IF1 60(Pre) Track-NQA primary path
Net1 IF2 90(Pre) Track-NQA backup path
Net1 IF3 100(Pre) Track-NQA backup path
Interface Backup
IP Floating Route

## Slide 38: Interface Backup and IP Floating Route
After interface backup is associated with BFD or NQA, if BFD or NQA detects that the primary link fails, a standby interface will be enabled. In this case, the active interface may still be physically up, so the related routing entries remain unchanged. As a result, data is still sent from the primary link.
IP floating routes can be associated with BFD or NQA to solve this problem.
IF1 (active)
IF2 (standby)
NQA
BFD
If the primary link fails, a standby interface is automatically enabled.
IP routing-table
Net1 IF1 primary path
Net1 IF2 backup path
The active interface is still in the up state.
Floating routes are unaware of faults, and routing entries remain unchanged.
Data forwarding fails.
IF1 (active)
IF2 (standby)
NQA
BFD
If the primary link fails, a standby interface is automatically enabled.
IP routing-table
Net1 IF1 Track
Net1 IF2 Track primary path
The active interface is still in the up state.
Floating routes can be associated with BFD or NQA to detect faults and switch routing entries.
The data forwarding path is switched, and data is forwarded properly.
IP floating routes are not associated with BFD or NQA
IP floating routes are associated with BFD or NQA
Interface Backup
IP Floating Route

## Slide 39
(True or false) Interface backup can be implemented only in active/standby mode, but not in load balancing mode.
  True
  False
Notes: 1. B

## Slide 40
Interface backup operates in either active/standby or load balancing mode. In active/standby mode, only one interface can work at a time. In load balancing mode, if the bandwidth of the active interface is insufficient, the standby interface can be used to forward traffic.
Interface backup can be associated with NQA, BFD, and routing tables to detect link quality and determine whether to perform an active/standby interface switchover.
Floating routes are typically used together with interface backup. Interface backup determines only whether interfaces can be enabled. Therefore, floating routes are required to guide data forwarding during Layer 3 forwarding.

## Slide 41
Link Reliability
Network Reliability
Service Reliability

## Slide 42: Network Reliability
If a fault occurs on the network, the fault may not be detected or rectified in a timely manner. Therefore, redundancy technologies are required.
Common redundancy technologies include stack, link aggregation, and VRRP.
VRRP is the most widely used network redundancy technology on egress devices or gateways.
VRRP
Stack
Link aggregation

## Slide 43: Overview of VRRP
Hosts are connected to external networks through gateways. If a single gateway fails, services will be interrupted for a long time. Adding egress gateways is a common method to improve system reliability. In this case, route selection among multiple egresses becomes essential.
VRRP groups multiple routing devices into a single virtual routing device. If a gateway fails, VRRP selects a new gateway to transmit data traffic, ensuring high network reliability.
Internet
VRRP
Only one device provides services externally.
Master
Backup
The master device forwards the traffic sent by hosts.
Internet
VRRP
Master
Backup -> Master
The downlink of the master device is disconnected, so the master device cannot provide gateway services.
The backup device becomes the new master device, and traffic is switched to it.
The backup device does not transmit traffic.
PC1
PC2
PC1
PC2
The master device fails.

## Slide 44: VRRP Fundamentals
VRRP technology aims to select a master device for packet forwarding. If the master device fails, traffic can be switched to the backup device in a timely manner. The following illustrates the VRRP mechanism:
VRID 1
Priority: 200
Virtual IP: IP1
Virtual MAC: MAC1
VRID 1
Priority: 100
Virtual IP: IP1
Virtual MAC: MAC1
Internet
VRID 1
Priority: 200
Virtual IP: IP1
Virtual MAC: MAC1
PC1
PC2
VRRP
Master
Backup
VRID 1
Priority: 100
Virtual IP: IP1
Virtual MAC: MAC1
Mac-address Table
MAC 1 IF1
IF2
High priority
GW: IP1
ARP: IP1 – MAC1
GW: IP1
ARP: IP1 – MAC1
The master device continuously sends VRRP packets.
The backup device listens to VRRP packets.
The switch learns the virtual MAC address.
IF1
Internet
PC1
PC2
VRRP
Master
Backup->Master
Mac-address Table
MAC 1 IF2
IF1
The master device fails and cannot send VRRP packets.
GW: IP1
ARP: IP1 – MAC1
GW: IP1
ARP: IP1 – MAC1
The new master device continuously sends VRRP packets.
The backup device determines that the master device fails and becomes the master device.
The switch learns the virtual MAC address again.
The main device fails.
SW
SW
IF2
Notes: VRRP mechanism:
  VRRP selects the master device based on the priorities of devices in a VRRP group. The master device sends gratuitous ARP packets to notify the devices or hosts that are connected to it of the virtual MAC address, and then starts forwarding packets.
  The master device periodically sends VRRP Advertisement packets to all backup devices in the VRRP group to advertise its configurations (such as the priority) and operating status.
  If the master device fails, the backup device with the highest priority is elected as the new master device.
  After a master/backup switchover, the new master device immediately sends gratuitous ARP packets carrying the virtual MAC and virtual IP addresses to allow the devices or hosts that are connected to it to update corresponding MAC entries. After the update is complete, user traffic is switched to the new master device, which is transparent to users.
  If the original master device recovers and it is the IP address owner (its priority is 255), it immediately switches to the Master state; whereas if the original master device recovers and its priority is lower than 255, it switches to the Backup state, and its original priority is restored.
  If the priority of a backup device is higher than that of a master device, VRRP determines whether to reelect a new master, depending on the backup device's working mode (preemption or non-preemption).
    Preemption mode: In this mode, a backup device preempts the master role if it has a higher priority than that of the current master.
    Non-preemption mode: In this mode, a backup device does not preempt the master role even if it has a higher priority than that of the current master, provided that the current master is working properly.

## Slide 45: VRRP Uplink Reliability
The master and backup devices in a VRRP group detect the master/backup status of each other. If the uplink fails, VRRP cannot detect the fault by default. As a result, packet loss occurs.
To solve this problem, associate VRRP with the uplink or set up a backup link between the master and backup devices.
Internet
PC1
PC2
VRRP
Master
Backup
The master still functions as the gateway and carries traffic.
The uplink fails.
Packet Loss occurs.
Internet
PC1
PC2
VRRP
Master
Backup
VRRP is associated with the uplink status.
Packet loss due to a VRRP uplink failure
VRRP uplink reliability solution
SW
SW
A backup link is set up between the master and backup devices.

## Slide 46: Associating VRRP with the Uplink Status
VRRP can monitor the uplink based on interfaces, BFD, NQA, or routes. If the uplink fails, VRRP triggers a master/backup switchover to switch traffic, preventing packet loss caused by the uplink failure.
Internet
PC1
PC2
VRRP
Master
Backup->Master
The uplink fails.
VRP monitors the uplink based on interfaces, BFD, NQA, or routes.
The uplink fails, so the master device automatically reduces its VRRP priority.
The backup detects that the VRRP priority of the master device reduces and then becomes the new master device.
Internet
PC1
PC2
VRRP
Backup
Master
Traffic is switched.
After a master/backup switchover
SW
SW
Notes: Interface-based link monitoring can monitor only the status of direct links and cannot detect the status of the remote network. Therefore, interface-based link monitoring has low accuracy but is easy to configure and does not require the peer device to support it.
BFD/NQA/route-based uplink monitoring can monitor direct or remote links. However, BFD/NQA sessions need to be configured on both ends, which has limitations.
After a master/backup VRRP switchover is performed, the switch learns MAC address entries again and forwards traffic to the master device based on the new MAC address table.

## Slide 47: VRRP Establishing a Dual-Device Interconnection Channel
On a live network, an additional link is deployed between the master and backup devices in a VRRP group to provide the following functions:
  Functions as the heartbeat line between the master and backup devices to help the backup device detect the status of the master device.
  Forwards traffic if the uplink or downlink fails.
Internet
PC1
PC2
VRRP
Master
Backup
Layer 3 interconnection channel
SW
The uplink fails.
Traffic is transmitted through the interconnection channel.
Internet
PC1
PC2
VRRP
Master
Backup
Layer 2 interconnection channel
SW
The downlink fails.
Traffic is transmitted through the interconnection channel.
Layer 2 interconnection channel transmitting traffic
Layer 3 interconnection channel transmitting traffic
Notes: On a live network, association between the uplink status and VRRP is often deployed together with dual-device interconnection channels.
An interconnection channel transmits traffic in the following two scenarios:
  A Layer 2 interconnection channel is deployed between the master and backup devices. If the downlink of the master device fails but the uplink is normal, traffic is sent from the backup device to the master device and then to the Internet through the Layer 2 channel. VRRP does not trigger a master/backup switchover, improving VRRP stability.
  A Layer 3 interconnection channel is deployed between the master and backup devices. When the downlink of the master device is normal but the uplink fails, traffic is sent to the master device, which then sends traffic to the backup device through the Layer 3 channel. The backup device forwards the traffic. In this scenario, VRRP does not trigger a master/backup switchover and uplink association is not required.

## Slide 48: Basic VRRP Configurations
Internet
VRRP
Master
Backup
The configuration roadmap is as follows:
  Configure a VRRP group.
  Set the device priority in a VRRP group.
system-view
interface [interface-type interface-num] //Enter the active interface view.
vrrp vrid [virtual-router-id] virtual-ip [virtual-address] //Create a VRRP group and configure a virtual IP address for the VRRP group.
vrrp vrid [virtual-router-id] priority [priority-value] //Configure the priority of the device in the VRRP group. By default, the priority value is 100. A larger value indicates a higher priority.
Perform basic VRRP configurations.

## Slide 49: VRRP Association Configuration
Associate VRRP with BFD:
Internet
VRRP
Master
Backup
The configuration roadmap is as follows:
  Configure VRRP association on an interface.
System-view
interface [interface-type interface-name] //Enter the active interface view.
vrrp vrid [virtual-router-id] track bfd-session session-name [bfd-session-name] increased | reduced [value] //Associate VRRP with BFD. If the BFD session is down, the VRRP priority is changed.
system-view
interface [interface-type interface-num] //Enter the active interface view.
vrrp vrid [virtual-router-id] track nqa [admin-name] [test-name] reduced [value-reduced ] //Associate VRRP with NQA. If the NQA session is down, the VRRP priority is changed.
Associate VRRP with NQA:
Associate VRRP with the interface status:
system-view
interface [interface-type interface-num] //Enter the active interface view.
vrrp vrid [virtual-router-id] track interface [interface-type interface-num] increased | reduced [value] //Associate the interface with NQA. When the interface is shut down, the VRRP priority is changed.

## Slide 50: Verifying the VRRP Configuration
During routine maintenance, run the following commands to check VRRP packet statistics and monitor the VRRP group running status.
system-view
display vrrp interface [interface-type interface-number ] [ virtual-router-id ] statistics //Display statistics about sent and received packets of a VRRP group.

## Slide 51
(Single-answer question) After a master/backup VRRP switchover is performed, which of the following entries are used to forward data to the new master device?
  ARP entries
  IP routing entries
  MAC address entries
  FIB entries
Notes: 1. C

## Slide 52
VRRP is typically deployed on gateways or egresses. Terminals are unaware of the master/backup VRRP switchover, and can access the network after the switchover.
After a master/backup VRRP switchover is performed, the switch connected to the VRRP devices guides traffic switching.
VRRP can be associated with multiple detection technologies to detect the uplink quality, which helps VRRP accurately perform a master/backup switchover.

## Slide 53
Link Reliability
Network Reliability
Service Reliability
  SAC
  SPR

## Slide 54: Service Reliability
In the cloud computing era, network reliability cannot meet user requirements. Users want to understand the live network status based on applications and adjust the network based on the application status.
Such requirement poses the following challenges to traditional networks:
  Traditional networks cannot accurately identify applications.
  Traditional networks cannot be adjusted based on applications.
To cope with the challenges, two technologies are developed:
  Smart Application Control (SAC): This technology can flexibly identify applications.
  Smart Policy Routing (SPR): This technology can switch forwarding paths based on the network or application status.

## Slide 55: Overview of SAC
Traditional networks are managed based on traffic. However, in the cloud computing era, services are becoming increasingly important. Networks need to be managed and monitored based on applications instead of Five-tuple information.
Traditional routing and switching devices cannot identify application-layer information. Therefore, it is difficult to manage networks based on applications. Smart Application Control (SAC) technology helps routing and switching devices identify classified applications.
SAC uses service awareness (SA) and first packet identification (FPI) technologies to detect and identify Layer 4 to Layer 7 information (such as HTTP and RTP) in packets.

## Slide 56: SAC Signature Database
Signature identification is a basic function of SA technology. Different applications typically use different protocols, and different application protocols have their own signatures. A signature that can identify a protocol is known as a signature code. The system analyzes service flows passing through a device, and compares the analysis result with the signature database on the device. It identifies an application by detecting the signature code in data packets.
SAC signature databases include FPI and SA signature databases. FPI signatures refer to signatures for identifying FPI applications, and SA signatures refer to signatures for identifying SA applications.
SAC working mechanism
SAC detection
Signature database
Audio/Video optimization
QoS policy
Traffic policy
Service traffic
Signature matching
Matching voice and video
Matching a user-defined service
Matching the web page service
Notes: The SAC signature database file can only be updated through upgrades and cannot be manually modified.
The SAC signature database can be updated in either of the following modes:
  Online update: The SAC signature database can be updated through the security center platform or intranet update server.
  Local update: The upgrade package is downloaded from the security center platform and uploaded to the device through FTP for the update of the SAC signature database.

## Slide 57: SAC Application Identification Process
During SAC application identification, the system checks whether an application is identified. If the application is not identified, the system checks the FPI signature database and SA signature database in sequence.
Network device
FPI signature database
Service traffic
Signature matching
SA signature database
Signature matching
Application identification record
SAC detection
Traffic is directly forwarded at Layer 3 if the application has been identified.
Voice
Video
Web page
Download
Forwarding table
Notes: After a packet enters the device, the device determines whether the corresponding application has been identified based on the 5-tuple information carried in the packet. If the application has been identified, the device forwards the packet at Layer 3 without identifying the application again. If the application has not been identified, the device performs the SAC application identification process. The device then processes the packet based on the SAC identification result and forwards the packet at Layer 3. The SAC application identification process is as follows: The device identifies an application based on the ACL rules defined in FPI. If the application cannot be identified, the device identifies the application based on the DNS entries defined in FPI. If the application still cannot be identified, the device identifies the application based on the protocol and port mapping table defined in FPI. If the application still cannot be identified, the device starts the SA identification process.

## Slide 58: SA
After receiving data, the device can use service awareness (SA) technology to match applications.
SA uses the SA signature database to detect services. The existing SA signature database is embedded with more than 6000 applications, ensuring a high identification rate for public applications. In most cases, the SA signature database can only be updated online or locally and cannot be manually modified.
SAC detection
Service traffic
Signature matching
SA behavior signature matching
Voice
Video
Web page
Matching conditions | Application
Domain name, server IP address, and protocol | Voice
Domain name, server IP address, and protocol | Web page
Domain name, server IP address, and protocol | Video

## Slide 59: FPI
There is a problem in matching applications based on the SA signature code. That is, the application corresponding to the first several packets may fail to be identified based on the SA signature code. As a result, the processing on the first and subsequent packets may be inconsistent. First packet identification (FPI) enables a device to identify an application by matching the first packet of a flow.
FPI identifies applications based on 5-tuple information, DSCP values, protocols, and DNS domain names. The system provides a predefined FPI signature database to help SAC identify applications. You can also define FPI applications to identify new applications.
SAC detection
Service traffic
Signature matching
FPI signature database
Voice
Video
Web page
Matching conditions | Application
Destination IP1, EF | Voice
Destination Port1, protocol number 6 | Web page
Destination IP2, AF4 | Video
Notes: FPI applications are classified into the following types:
  Predefined and user-defined FPI applications based on the protocol and port number: These two types of applications are identified using entries that are generated based on the protocol and port number carried in packets. The difference is as follows: Packets of a predefined FPI application contain common protocols and port numbers, while packets of a user-defined FPI application contain the protocols and ports that you define.
  Predefined and user-defined FPI applications based on the DNS domain name: These two types of applications are identified using DNS entries generated through association between FPI and DNS. The difference is as follows: Packets of a predefined FPI application contain common DNS domain names, while packets of a user-defined FPI application contain the DNS domain names that you define.
  User-defined FPI application based on 5-tuple and DSCP information. This application is identified based on the user-defined 5-tuple and DSCP information using advanced ACL rules.
Identification process of FPI applications based on the DNS domain name
  FPI applications based on the DNS domain name are identified using DNS entries generated through association between FPI and DNS. The FPI signature database contains the mappings between domain names and applications. DNS response packets contain the mappings between domain names and IP addresses. Based on the mappings, a device generates DNS entries, which contain the mappings between IP addresses and applications. The device searches for DNS entries based on the IP address carried in the application protocol packets to identify the corresponding application.

## Slide 60: Configuring SAC and Verifying the SAC Configuration
To use the SAC function, you need to purchase the corresponding license and enable the in-depth security protection function of the device. After in-depth security protection is enabled, the system automatically loads the built-in signature database file.
Enable SAC.
After enabling SAC, verify the SAC configuration.
system-view
engine enable //Enable the in-depth security protection function. After the function is enabled, application identification can be performed 3 minutes later.
system-view
display sa information //Check the SA status. If the SA status is enabled, in-depth security protection has been enabled.

## Slide 61
(True or false) The signature database used by the FPI technology can be manually modified, but the signature database used by the SA technology cannot.
  True
  False
Notes: 1. A

## Slide 62
The main purpose of the SAC technology is to distinguish different services in traffic and help other modules control traffic based on different services.
SAC consists of the SA and FPI modules.
The FPI module can identify services based on the traffic characteristics such as the 5-tuple, protocol number, and DSCP value. In addition, the FPI module supports the user-defined signature database.
The SA module identifies services based on application behaviors and the application-layer signature codes of data packets. The SA signature database does not support user-defined signature databases.

## Slide 63
Link Reliability
Network Reliability
Service Reliability
  SAC
  SPR

## Slide 64: Overview of SPR
In the cloud computing era, more users shift their attention from network connectivity to service availability, such as service response speed and service quality. However, traditional networks cannot detect link quality and service requirements, resulting in poor user experience.
Smart Policy Routing (SPR) addresses this problem. It actively detects the link quality and matches service requirements to select an optimal link to forward service data. SPR prevents network blackholes and flappings.
NQA
IP FPM
HQ
Branch
NQA
IP FPM
SRP deployment
SRP deployment

## Slide 65: SPR Service Differentiation
SPR differentiates traffic based on the protocol type, packet application, and packet information.
Different link quality parameter thresholds can be set for different services. You can set the delay (D), jitter (J), packet loss rate (L), and composite measure indicator (CMI).
CMI is calculated based on the delay, jitter, and packet loss rate.
SPR selects routes based on the CMI.
NQA
IP FPM
Branch
NQA
IP FPM
SPR module
TCP, UDP, GRE…
Source IP, Source Port, Destination IP…
DSCP, VPN, TCP-flag…
Based on the protocol type
Based on the packet application
Based on packet information
Notes: SPR classifies services based on the following attributes:
  Protocol types: IP, TCP, UDP, GRE, IGMP, IPINIP, OSPF, and ICMP
  Packet applications: DSCP, ToS, IP precedence, fragment, VPN, and TCP-flag
  Packet fields: Source IP Address, Destination IP Address, Protocol, Source Port, Destination Port, Source IP Prefix, Destination IP Prefix
When SPR selects routes for services based on the NQA detection result, the CMI is calculated using the following formula:
  CMI = 9000 – CMI-method. The default value of CMI-method is D + J + L.
  If NQA is used, a larger CMI value indicates better link quality.
When SPR selects routes for services based on the IP FPM detection result, the CMI is calculated using the following formula:
  CMI = D + J + L
  If IP FPM is used, a smaller CMI value indicates better link quality.

## Slide 66: SPR Detection Link and Link Group
SPR obtains quality indicators of detection links through probes (NQA or IP FPM) and then selects an optimal link.
A link group can contain one or more detection links.
SPR defines three roles for links: primary link group, backup link group, and best-effort link. When no suitable link is available in the primary and backup link groups, SPR activates the best-effort link to forward service data.
Network device
Internet
MPLS
LTE
Primary link group
Backup link group
Link detection
Link detection
Link detection

## Slide 67: SPR Link Selection
SPR periodically obtains the NQA or IP FPM detection result to determine whether a link meets service requirements. If the link does not meet service requirements, a link switchover is triggered.
The SPR link selection process is as follows:
Link selection based on the NQA test result
Link selection based on the IP FPM test result
The NQA detection result is read.
Is there a primary link whose quality meets service requirements?
Is there a backup link whose quality meets service requirements?
Is the CMI of the primary and backup link groups 0?
The best-effort link is started.
End
The link with the optimal CMI in the primary link group is used.
The link with the optimal CMI in the backup link group is used.
The link with the optimal CMI in the primary and backup link groups is used.
Yes
Yes
No
No
No
Yes
The IP FPM detection result is read.
Is there a primary link whose quality meets service requirements?
Is there a backup link whose quality meets service requirements?
Is the CMI of the primary and backup link groups 9000?
End
The link with the optimal CMI in the primary link group is used.
The link with the optimal CMI in the backup link group is used.
The link with the optimal CMI in the primary and backup link groups is used.
Yes
Yes
No
No
No
Yes
Notes: When a network is unstable, SPR triggers link switchovers frequently, which degrades service experience. SPR provides the flapping suppression function to address this problem.
The flapping suppression function is disabled by default, and the flapping suppression period is configurable. After traffic is switched to a new link, SPR starts the flapping suppression timer. Within a flapping suppression period, SPR does not perform a link switchover even if it does not obtain the NQA test result indicating that the link meets service requirements within a switchover period. After the flapping suppression timer expires, if SPR still does not obtain the NQA test result indicating that the link meets service requirements within a switchover period, SPR performs a link switchover. If SPR obtains the NQA test result indicating that the link meets service requirements within a switchover period, SPR retains traffic on the link without performing a link switchover.

## Slide 68: Using iMaster NCE to Implement SPR
During SPR deployment through iMaster NCE, to improve the site specifications on the entire network, separation between sites and application policies and traffic-triggered link selection are used together.
iMaster NCE maintains site adjacency information and application policies, and SPR is configured on routers. Traffic-triggered link selection allows for on-demand generation of SPR configurations. This prevents a large number of configurations from being created on the device and reduces the impact of link selection (based on IP FPM) on the CPU, significantly reducing the burden on the device.
iMaster NCE can use SAC to classify service traffic based on applications.
Site adjacency list
Application policy table
Site policy table
Triggering IP FPM link selection
IP FPM link selection
Generated dynamically
Site adjacency list
Application policy table
iMaster NCE
Network device

## Slide 69: Setting SPR Routing Parameters
Set SPR routing parameters.
NQA
IP FPM
SPR module
To configure SPR, set SPR routing parameters and associate SPR with services.
The configuration roadmap is as follows:
  Configure an NQA or IP FPM test instance.
  Bind the test instance to an interface group.
IF1 (Active)
IF2 (Standby)
system-view
smart-policy-route //Create SPR.
prober [interface-type interface-num] nqa [admin-name] [test-name] //Configure a detection link in SPR and associate it with an NQA test instance.
nqa-ipfpm link-fail-detect interval [interval-time] count [detect-count] //(Optional) The device is configured to trigger an SPR-based switchover after an IP FPM session fails.
link-group [name] //Create a link group.
link-member [interface-type interface-num] //Add the specified interface to the link group.

## Slide 70: Associating SPR with Services
Associate SPR with services:
NQA
IP FPM
SPR module
To configure SPR, set SPR routing parameters and associate SPR with services.
The configuration roadmap is as follows:
  Configure an SPR service profile.
  Configure SPR interested traffic.
  Configure the primary link group.
IF1 (active)
IF2 (standby)
system-view
smart-policy-route //Create SPR.
service-map [name] //Create an SPR service profile.
match [acl | application] [acl-num | app-name] //Create interested traffic. The interested traffic can be defined using an ACL or SAC.
set link-group [name] //Configure the primary link.

## Slide 71: Verifying the SPR Configuration
After the SPR configuration is complete, run the following commands to check the configuration:
display smart-policy-route //Check the SPR routing configuration.
display smart-policy-route service-map [ name ] //Check the service profile configuration.
display smart-policy-route link-state [ interface-type interface-number ] //Check the detection link status.
display smart-policy-route nqa-server link-state //Check the NQA server link status.

## Slide 72
(Single-answer question) Which of the following is used by SPR to determine the optimal path?
  Jitter
  Delay
  Packet loss rate
  CMI
Notes: 1. D

## Slide 73
SPR is a type of policy-based routing. It can be associated with NQA and IP FPM so that a path can be quickly selected when a network change occurs.
SPR selects the optimal path based on the CMI. The CMI calculation method used when NQA is used to detect link quality is different from that used when IP FPM is used to detect link quality.
SPR can be implemented based on iMaster NCE. Services can be delivered through iMaster NCE, making SPR more convenient.

## Slide 74
There are many HA technologies. In the past, HA technologies focused on the high reliability of the network layer. With the development of cloud computing, there are more and more service HA requirements.
New technologies, such as IP FPM, SAC, and SPR, are developed to meet service HA requirements.
Traditional HA technologies, such as VRRP, BFD, and interface backup, are used together with service HA technologies to improve network reliability.