## Slide 1
Datacom
V1.0
He Junjian/WX580230
2020.03.06
Shi Miaomiao/swx791350
Update

## Slide 2: Enterprise Bearer WAN Architecture and Key Technologies

## Slide 3
The IP bearer WAN, which usually covers a country, is a data communication network that provides interconnection between multiple LANs or branch networks across regions.
This course introduces the concepts, principles, and applications of the enterprise bearer WAN's typical architecture, bearer technologies, VPN services, traffic optimization, SLA, reliability, and network management and analysis. To introduce these key aspects, this course uses a large enterprise with three data centers in two cities and multiple branches in different regions as an example.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the typical architecture of the bearer WAN.
  Describe the basic concepts of Multiprotocol Label Switching (MPLS), Segment Routing-Multiprotocol Label Switching (SR-MPLS), and Segment Routing IPv6 (SRv6).
  Describe the principles of WAN traffic optimization.
  Describe the SLA model and packet processing flow.
  Describe the network reliability design.
  Describe the key protocols for network management and analysis.

## Slide 5
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 6: Typical Architecture of the Bearer WAN
WAN-P
WAN-P
DC-P
RR
DC-P
DC-P
RR
DC-PE
DC-PE
DC-PE
WAN-P
DC-CE
DC-CE
Data center
Data center
Data center
DC-CE
Enterprise branch
Enterprise branch
BR-PE
BR-CE
BR-PE
BR-CE
City A
City A
City B
City C
City D
DC-P: builds a high-speed interconnection network with the two-city three-center architecture.
DC-PE: aggregates data center or intra-city services.
DC-CE: functions as the data center access device.
WAN-P: aggregates traffic from the uplinks of provincial branches.
RR: reflects regional routes on the bearer WAN.
BR-PE: functions as the branch edge device on the bearer WAN.
BR-CE: functions as the branch access device.
* Note: It is recommended that two WAN-Ps be deployed for the dual-plane bearer WAN. Here, only one WAN-P is displayed in the topology.
Notes: The Ps for intra-city data center are directly connected using WDM or bare optical fibers. The link bandwidth can reach 10 Gbit/s. To reduce costs, consider connecting local data centers with remote data centers through carriers' MSTP links.

## Slide 7: Typical Architecture of the Bearer WAN
The typical architecture of a bearer WAN is divided into three layers: access layer, aggregation layer, and core layer.
Aggregation layer
Core layer
Access layer
Access layer (CE-PE):
Provides access for data centers in different cities.
Provides access for branches in different cities.
Provides access for external services in different cities.
Aggregation layer (PE-P):
Aggregates and transmits different types of services to the bearer WAN based on physical locations.
Core layer (P):
Generally adopts the full-mesh + dual-plane architecture.
Provides stable, reliable high-speed traffic forwarding between regions.

## Slide 8: Technologies Used by the Typical Bearer WAN Architecture
For CEs accessing the same PE, VPNs are used to isolate services:
L2VPN: Layer 2 communication
L3VPN: Layer 3 communication
Data forwarding:
MPLS or IPv6 forwarding
CE
CE
P
PE
PE
PE
Service 1
P
CE
CE
Bearer WAN
Service 2
Service 2
Service 1
P
P
Service tunnels are established between PEs for VPN service recursion. For example:
MPLS LDP tunnels
MPLS TE tunnels
SR-MPLS BE/TE tunnels
SRv6 BE tunnels

## Slide 9
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 10: MPLS Overview
MPLS is located between the data link layer and the network layer in the TCP/IP protocol stack and can provide services for all network layers.
An MPLS header is added between a data-link-layer header and a network-layer header, and data can be forwarded quickly based on the MPLS header.
MPLS label-based forwarding
MPLS label-based forwarding
IP-based forwarding
IP network
IP network
IP
packet
MPLS
header
Ethernet
header
MPLS
SRv6
SR-MPLS

## Slide 11: MPLS Terms (1)
MPLS domain: consists of a series of consecutive network devices that run MPLS.
Label switching router (LSR): a routing device, such as a router or switch, that runs MPLS. An LSR that resides at the edge of an MPLS domain and connects to a non-MPLS network is called a label edge router (LER). An LSR that resides inside an MPLS domain is called a core LSR.
The path that MPLS packets take in an MPLS network is called a label switched path (LSP). The LSP is a unidirectional path that transmits traffic from the ingress to the egress.
The start node of an LSP is called the ingress, an intermediate node of the LSP is called the transit node, and the end node of the LSP is called the egress. An LSP has one ingress, one egress, and zero, one, or multiple transit nodes.
MPLS domain
LER
Core LSR
LER
IP network
IP network
IP packet
MPLS header
Ethernet header
Ingress
Transit
Egress
MPLS
SRv6
SR-MPLS

## Slide 12: MPLS Terms (2)
Forwarding equivalence class (FEC): a set of packets with similar or identical characteristics and forwarded in the same way by LSRs. In traditional IP forwarding that uses the longest match algorithm, all packets that match the same route belong to the same FEC.
An LSP is composed of an ingress LSR, an egress LSR, and a variable number of transit LSRs. Therefore, an LSP can be considered as an ordered set of these LSRs.
An LSP must be established before a packet is forwarded; otherwise, the packet fails to traverse an MPLS domain.
An LSP is a unidirectional path from the start point to the end point. If bidirectional data communication is required, an LSP for return traffic needs to be established between the two ends.
MPLS domain
IP network
10.0.1.0/24
10.0.2.0/24
R1
R2
R3
R4
R5
R6
R7
IP network
IP network
Purpose: 10.0.1.1
Purpose: 10.0.2.1
R8
LSP1
LSP2
IP packet
Ethernet header
MPLS
SRv6
SR-MPLS
Notes: For more information about MPLS, see HCIP-Datacom-Advanced Routing & Switching Technology.

## Slide 13: MPLS Terms (3)
LSPs can be statically configured or dynamically established.
There are two common protocols for dynamically establishing LSPs: LDP and Resource Reservation Protocol-Traffic Engineering (RSVP-TE).
LDP: used to establish common LSPs
LDP distributes labels from downstream routers to upstream routers based on the routing table to set up common LSPs.
A common LSP is usually the shortest path calculated by an IGP, which does not factor in aspects such as bandwidth, tunnel protection, and traffic optimization.
RSVP-TE: used to establish CR-LSPs
RSVP-TE establishes tunnels by applying for and reserving tunnel resources end to end.
An LSP that is set up based on bandwidth or path constraints is called a constraint-based routed label switched path (CR-LSP).
R1
R2
R3
Hop-by-hop resource reservation and label distribution
MPLS TE tunnel (CR-LSP)
Tunnel resource reservation
Tunnel resource reservation
R1
R2
R3
MPLS LSP
Downstream-to-upstream label distribution
MPLS
SRv6
SR-MPLS

## Slide 14: MPLS LDP Overview
LDP is a control protocol of MPLS and provides functions such as FEC classification, label distribution, and LSP establishment and maintenance. LDP defines the messages used in label distribution as well as the message processing procedures.
LDP is easy to configure and maintain and is widely used to create LSPs in BGP/MPLS IP VPN scenarios. As shown in the figure, the carrier builds a bearer WAN for MPLS VPNs to provide inter-provincial L3VPN services for customers.
MPLS LDP LSPs are established based on the shortest IP paths and do not support the planning of tunnel forwarding paths.
Bearer WAN for MPLS VPNs
Company A
Network in province X
Company B
Network in province X
Company B
Network in province Z
Company A
Network in province Y
MPLS
SRv6
SR-MPLS

## Slide 15: MPLS TE Overview
MPLS TE, as its name suggests, is a combination of MPLS and TE. It provides functions such as path planning, traffic optimization, and fault protection for MPLS VPN services.
Compared with MPLS LDP, MPLS TE enhances VPN traffic control and protection.
Path planning
Traffic optimization
Fault protection
Different paths are planned for different services.
Traffic is evenly distributed to idle links when unbalanced traffic distribution occurs due to major events, such as live broadcast.
Fast protection switching is performed in the case of a device or link fault.
MPLS
SRv6
SR-MPLS

## Slide 16: MPLS TE Tunnel
MPLS TE often associates multiple LSPs with a virtual tunnel interface, and such a group of LSPs is called an MPLS TE tunnel.
An MPLS TE tunnel provides SLA assurance, but requires complex configuration and manual planning.
R1
R2
R3
R4
Primary path
Backup path
[R1] interface tunnel1
[R1-Tunnel1] ip address …
[R1-Tunnel1] tunnel-protocol mpls te
[R1-Tunnel1] destination R4
[R1-Tunnel1] mpls te bandwidth 50M
…
MPLS TE
MPLS
SRv6
SR-MPLS

## Slide 17: Issues with MPLS LDP and RSVP-TE
MPLS LDP
RSVP-TE
R1
R2
R4
R3
IGP
LDP itself does not have the path computation capability and requires an IGP for path computation.
Both the IGP and LDP need to be deployed for the control plane, and devices need to exchange a large number of packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
If LDP-IGP synchronization is not achieved, data forwarding may fail.
RSVP-TE is complex to configure and does not support load balancing.
To implement TE, devices need to exchange a large number of RSVP packets to maintain neighbor relationships and path states, wasting link bandwidth and device resources.
RSVP-TE uses a distributed architecture, so that each device only knows its own state and needs to exchange signaling packets with other devices.
LDP
LDP
LDP
LDP
IGP
IGP
IGP
R1
R2
R4
R3
RSVP response
RSVP response
RSVP request
RSVP request
How can we simplify the control plane?
MPLS
SRv6
SR-MPLS

## Slide 18: SR-MPLS Overview
SR is designed to forward data packets on a network using the source routing model.
SR-MPLS, as its name suggests, is SR based on MPLS label forwarding.
2
400
800
3
R4
R6
R8
R1
R2
R3
R5
R7
400
600
800
Source routing:
  The source node selects a path and pushes an ordered label stack into the packet.
  Other nodes on the network forward the packet according to the label stack encapsulated into the packet.
SR has the following characteristics:
  Extends existing protocols (e.g. IGP) to facilitate network evolution.
  Supports both centralized controller-based control and distributed forwarder-based control, providing a balance between the two control modes.
  Enables networks to quickly interact with upper-layer applications through the source routing technology.
600
500
700
Label stack
MPLS
SRv6
SR-MPLS
1

## Slide 19: SR-MPLS BE and SR-MPLS TE
The SR-MPLS tunneling technology can be implemented in either SR-MPLS BE or SR-MPLS TE mode.
SR-MPLS BE
Forwarding path: Similar to an MPLS LDP LSP, an SR-MPLS BE LSP is calculated using the IGP shortest path first (SPF) algorithm. An SR-MPLS BE LSP has only one label layer (destination node).
In the production environment, SR-MPLS BE is generally used as the DR solution for SR-MPLS TE. For example, if a controller fault causes a tunnel delivery failure, the IGP can be used to generate forwarding tunnels.
SR-MPLS TE
Forwarding path: An SR-MPLS TE path is created using SR based on TE constraints. An SR-MPLS TE tunnel generally uses multiple layers of labels to implement path control and supports primary and backup paths.
SR-MPLS TE is usually used with a controller. After the controller globally computes a path, it delivers a label stack to the corresponding ingress.
Shortest path
Primary path
400
600
Packet
600
500
400
600
500
500
600
Packet
Constrained path
Backup path
SR-MPLS TE Tunel
400
Label stack
Label stack
MPLS
SRv6
SR-MPLS

## Slide 20: SR-MPLS Policy
The SR-MPLS Policy, also called the SR-MPLS TE Policy, is one of the mainstream SR-MPLS implementation modes.
As defined in the corresponding RFC, an SR Policy is identified by <headend, color, endpoint> and contains multiple candidate paths.
SR Policy
Candidate path 1
Preference 200
Candidate path 2
Preference 100
Segment list 1
Weight
Segment list 2
Weight
Segment list 1
Weight
Primary path
Backup path
<Headend, color, endpoint>
SR Policy model
Green
Controller
BGP SR Policy
SR Policy application scenario
The controller collects information such as the global topology, network bandwidth, and link delay. After computing an SR Policy path based on service requirements, the controller uses BGP to deliver the path to the ingress.
A candidate path can contain multiple segment lists, and load balancing can be implemented among these segment lists based on weights.
Candidate paths work in primary/backup mode based on their preferences.
MPLS
SRv6
SR-MPLS
Notes: Based on MPLS and IPv6 forwarding technologies, SR Policies can be classified into SR-MPLS and SRv6 Policies.

## Slide 21: SRv6 Overview
SRv6 is designed to forward data packets on an IPv6 network using the source routing model.
Both SRv6 and SR-MPLS comply with the SR architecture. Their main difference lies in data plane instructions. The former is based on the IPv6 network and uses IPv6 addresses as instructions. In contrast, the latter is based on the MPLS network and uses MPLS labels as instructions.
1
2
FC00::4
3
R4
R6
R8
R1
R2
R3
R5
R7
FC00::8
Source routing:
The source node selects a path and pushes an ordered label stack into the packet.
Other nodes on the network forward the packet according to the label stack encapsulated into the packet.
Label stack
FC00::6
FC00::5
FC00::7
FC00::8
FC00::6
FC00::4
MPLS
SRv6
SR-MPLS

## Slide 22: SRv6 Extension Header
SRv6 adds a segment routing header (SRH) to IPv6 packets. The SRH contains an explicit IPv6 address stack. During the forwarding process, SRv6 nodes continuously update the destination address and offset the address stack to complete hop-by-hop forwarding.
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type=4 |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List[0] (128-bit IPv6 address) |  |  |  | 
Segment List[1] (128-bit IPv6 address) |  |  |  | 
Segment List[2] (128-bit IPv6 address) |  |  |  | 
Optional TLV Objects (Variable) |  |  |  | 
IPv6 Payload |  |  |  | 
IPv6 address stack
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)
Offset pointer: The value decrements by 1 hop by hop from bottom to top.
The next-hop IPv6 address is changed based on the pointer.
MPLS
SRv6
SR-MPLS

## Slide 23: Summary: WAN Bearer Technologies
WAN-P
WAN-P
DC-P
RR
DC-P
DC-P
RR
DC-PE
DC-PE
DC-PE
WAN-P
DC-CE
DC-CE
Data center
Data center
Data center
DC-CE
Enterprise branch
Enterprise branch
BR-PE
BR-CE
BR-PE
BR-CE
Enterprise bearer WANs can be roughly classified into two types: MPLS network and IPv6 network.
MPLS network:
  MPLS LDP
  MPLS TE
  SR-MPLS
IPv6 network:
  SRv6
Bearer WAN
MPLS
SRv6
SR-MPLS

## Slide 24
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
  WAN VPN Overview
  Tunnel Management Overview
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 25: VPN Classification
The VPN technology is widely used as a virtual private tunneling technology. VPN can be classified into various types from different perspectives. For example, VPN can be classified into Layer 3 VPN (L3VPN), Layer 2 VPN (L2VPN), and Virtual Private Dial-up Network (VPDN) by implementation layer.
VPWS, VPLS, and BGP/MPLS IP VPN are more widely used on bearer WANs.
GRE VPN and IPsec VPN, which are mainly used on the Internet, are beyond the scope of this course.
VPN Classification
L2 VPN
VPWS
VPLS
VPDN
L3VPN
BGP/MPLS IP VPN
GRE VPN
IPsec VPN
Covered in this course
Notes: Traditional switching networks, such as asynchronous transfer mode (ATM) and frame relay (FR) networks, are integrated with IP or MPLS networks. As a result, Layer 2 virtual private network (L2VPN) emerges. L2VPN includes Virtual Pseudo Wire Service (VPWS) and Virtual Private LAN Service (VPLS):
  VPWS is a P2P L2VPN technology that emulates the basic behaviors and characteristics of services such as ATM and frame relay.
  VPLS provides P2MP L2VPN services so that sites are connected as if they were on the same LAN.
Virtual Private Dial-up Network (VPDN) is a virtual private network constructed on the public network. It uses a dedicated network encryption communication protocol to provide access services for international organizations and mobile workforce of enterprises. There are multiple VPDN tunneling protocols, among which Layer Two Tunneling Protocol (L2TP) is the most widely used. Strictly speaking, L2TP is also a type of L2VPN, but its network structure and protocol design are quite different from those of other types of L2VPN. In addition, L2TP uses the dial-up mode. Therefore, L2TP is classified as VPDN.
L3VPN is also called Virtual Private Routing Network (VPRN), including RFC 2547-based BGP/MPLS IP VPN as well as IPsec VPN and GRE VPN carried over IPsec or GRE tunnels.

## Slide 26: WAN VPN Service Overview
An enterprise establishes a bearer WAN to provide wide-area interconnection for its internal and external services, such as production, office, external connection, and test services. These services are logically isolated but share the same physical network resources. Therefore, these services are called WAN VPN services.
WAN VPN can be classified into L2VPN and L3VPN.
Traditional L2VPN and L3VPN technologies
Traditional L2VPN includes VPLS and VPWS, which can use LDP or BGP to establish virtual links.
Traditional L3VPN uses VPN instances to isolate services and uses BGP VPNv4/v6 to transmit Layer 3 information.
EVPN
EVPN provides both Layer 2 and Layer 3 capabilities and functions as a control plane protocol to transmit Layer 2 and Layer 3 information (MAC/IP addresses). EVPN can be used together with the traditional VPN technology.
EVPN supports EVPN VPLS, EVPN VPWS, EVPN L3VPN, etc.
PE
PE
L3VPN
L2VPN
BGP VPNv4
BGP l2vpn-ad
BGP VPNv6
PE
PE
L3VPN
L2VPN
BGP EVPN
BGP EVPN
Notes: A traditional L2VPN does not have any control plane and does not transmit service route information (MAC addresses). It uses BGP as the signaling protocol to establish VCs.
For details about VPN classification, see the book SRv6 Network Programming: Ushering in a New Era of IP Networks.

## Slide 27: Traditional WAN L2VPN Overview
The traditional WAN L2VPN is based on the MPLS network. VPWS provides a point-to-point Layer 2 network, and VPLS provides a point-to-multipoint Layer 2 network.
The basic MPLS L2VPN architecture is composed of the attachment circuit (AC), VC, and tunnel.
  AC: independent physical or virtual circuit connecting a CE and a PE. An AC interface can be either a physical or logical interface.
  VC: logical connection between two PEs. A VC is established using a signaling protocol, such as BGP AD.
  Tunnel: used to transparently transmit service data. Typical tunnels include MPLS LDP tunnels and MPLS TE tunnels.
VPLS and VPWS are widely used on carrier networks to provide MPLS Layer 2 private line services for enterprises.
PEA
PEB
MPLS domain
CEB
CEA
AC
AC
VC
P
Tunnel
Notes: VCs are also called pseudo wires (PWs) in some documents.

## Slide 28: Traditional WAN L3VPN Overview
Traditional WAN L3VPN generally refers to BGP/MPLS L3VPN.
It distinguishes the control plane from the data plane. The control plane uses MP-BGP to advertise VPN routes, and the data plane uses MPLS LSPs to forward VPN packets.
BGP/MPLS L3VPN is widely used on carrier networks to provide MPLS Layer 3 private line services for enterprises.
MPLS domain
P
PE2
PE1
CE1
192.168.1.0/24
Site A of user X
192.168.2.0/24
CE2
192.168.2.0/24
Site B of user X
192.168.1.0/24
1
2
Route transmission through BGP
MPLS packet forwarding
Control plane
Data plane

## Slide 29: WAN EVPN Overview
EVPN was initially designed as an L2VPN technology based on BGP extensions. With the development of protocol extensions, EVPN can also support L3VPN now.
EVPN can well serve as the control plane protocol for WAN VPN. It can be used with traditional VPN technologies to provide EVPN VPLS, EVPN VPWS, and EVPN L3VPN.
VPLS
VPWS
L3VPN
Traditional WAN VPN
EVPN
VPLS
EVPN
VPWS
EVPN
L3VPN
RFC7432
Basic Standard
RFC8214
draft-ietf-bess-evpn-prefix-advertisement-05
EVPN
The EVPN standard is gradually maturing, unifying all services on the control plane.

## Slide 30: WAN EVPN Application
On a WAN, EVPN can be used with multiple tunneling technologies to support multiple application scenarios.
EVPN, as a control plane protocol, can work with MPLS LDP, MPLS TE, SR-MPLS, and SRv6 tunnels, as shown in the figure.
On Huawei devices, EVPN L2VPN and L3VPN services share the same address family.
WAN
P
P
PE
PE
CE
CE
EVPN L3VPNv4
EVPN L3VPNv6
EVPN VPLS
EVPN VPWS
MPLS LDP
MPLS TE
SR-MPLS
SRv6
[Router] bgp 100
[Router-bgp] l2vpn-family evpn
…

## Slide 31: Summary: WAN VPN
The VPN technology is widely used in various enterprise scenarios. VPNs can be built over either the Internet or a private network.
L2VPN (VPLS and VPWS), L3VPN (BGP/MPLS IP VPN), and L2/L3 EVPN can be deployed on a bearer WAN built by an enterprise.
EVPN, as a control plane protocol, can work with different bearer technologies (such as MPLS LDP, MPLS TE, SR-MPLS, and SRv6) to provide integrated and unified VPN services for enterprises.
When multiple tunneling technologies are deployed on an enterprise bearer WAN, VPNs must recurse to tunnels based on tunnel policies.

## Slide 32
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
  WAN VPN Overview
  Tunnel Management Overview
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 33: Tunnel Management
Huawei devices use a tunnel management (TNLM) module to manage tunnels. It selects a certain tunnel for an application according to specific configurations and notifies the application of the tunnel's status.
Common VPN tunnels include LSPs (MPLS LDP), MPLS TE tunnels, GRE tunnels, SR-MPLS Policies, and SRv6 Policies.
Tunnel management configuration includes two parts: configuring a tunnel policy and applying a tunnel policy to a VPN.
MPLS LDP
MPLS TE
SR-MPLS
SRv6
Tunnel policy 1
Tunnel policy 2
VPN1
VPN2
Application
Application
Notes: GRE: GRE can be applied to both L2VPN and L3VPN. Generally, the bearer WAN for MPLS VPN uses LSPs as public network tunnels. If the bearer WAN (P devices) has only IP functions but not MPLS functions, and the PEs at the network edge have MPLS functions, the LSPs cannot be used as public network tunnels. In this case, GRE tunnels can be used to replace LSPs to provide L3VPN or L2VPN solutions on the bearer WAN.
SR-MPLS Policy: a type of SR-MPLS tunnel.
SRv6 Policy: a type of SRv6 tunnel.
You can configure tunnel policies or tunnel policy selectors for tunnel management. This course uses tunnel policy configuration as an example. Tunnel policy selectors apply to inter-AS VPN scenarios. For details, see the product documentation for NetEngine products.

## Slide 34: Configuring a Tunnel Policy
A tunnel policy determines the types and sequence of tunnels to be selected.
By default, a VPN service recurses only to one LSP. If multiple LSPs are available, a tunnel policy can be used for load balancing among these LSPs.
In this example, to implement load balancing between MPLS LDP LSPs and TE tunnels, you need to configure a tunnel policy for the VPN and apply the tunnel policy to the VPN. The tunnel policy policy1 requires tunnels to be selected in the sequence of first CR-LSPs and then LSPs, and the number of tunnels for load balancing is 2. The system preferentially selects two CR-LSPs. If only one or no CR-LSP is available on the network, the system selects one or two LSPs, respectively, for service transmission. In the scenario where only one CR-LSP is available, it works together with the selected LSP.
MPLS LDP
MPLS TE
PE2
PE1
[PE1] tunnel-policy policy1
[PE1-tunnel-policy-policy1] tunnel select-seq cr-lsp lsp load-balance-number 2
Notes: The configuration of tunnel policy parameters involves many details. For example, CR-LSP-based tunnels include RSVP-TE tunnels and SR-MPLS TE tunnels. The system determines the priorities of these tunnels based on their up time. For details, see "VPN Tunnel Management Configuration" in the product documentation for Huawei NetEngine routers.

## Slide 35: Applying a Tunnel Policy to a VPN
After being configured, a tunnel policy needs to be applied to a VPN. The mode in which a tunnel policy is applied to a VPN varies according to the VPN type.
This example shows how to apply a tunnel policy to an L3VPNv4 instance.
MPLS LDP
MPLS TE
PE2
PE1
[PE1] ip vpn-instance vpn1
[PE1-vpn-instance-vpnb] ipv4-family
[PE1-vpn-instance-vpnb-af-ipv4] tnl-policy policy1
Notes: For the application of other types of VPN, such as VPNv6, L2VPN, and EVPN, see the product documentation for NetEngine routers.

## Slide 36: Extension: SR Policy-based Traffic Diversion
Tunnel policies are designed by Huawei for VPN service recursion in the MPLS era. They effectively decouple tunnel establishment from tunnel selection. In this way, the traffic of a VPN can be directed to multiple tunnels for load balancing. After the SR technology is introduced, the implementation mode changes. SR Policies integrate tunnel establishment (SR forwarding path) and tunnel policies (color-based traffic diversion by default). SR Policies cannot be selected together with other types of tunnels.
An SR Policy is identified by <headend, color, endpoint> and can contain multiple forwarding paths. A VPN service selects an SR Policy based on the color attribute.
<R1, Green, R4>
There are two SR Policies (blue and green) between R1 and R4.
R1 queries its VPN routing table after receiving traffic from the CE.
If the color of the corresponding VPN route is Blue, R1 selects an SR Policy with the same color for route recursion.
<R1, Blue, R4>
R1
R4
CE
VPN route
(Blue)
Notes: For details, see "SR Policy" in 2. Terminology in RFC 8402.
SR Policy traffic diversion can be based on the binding SID, color, and DSCP value. Details are not provided here.

## Slide 37
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 38: Network Congestion Background
The network computes forwarding paths based on bandwidth. The link from Router C to Router D is the shortest forwarding path. The rate of service traffic from Router C to Router D exceeds the link bandwidth, and packet loss occurs. Although other links are idle, the algorithm still selects the shortest path for traffic forwarding. From a global perspective, the optimal traffic forwarding path is C -> A -> D in this situation.
Used bandwidth/Total bandwidth
Global path computation for optimal tunnel path adjustment:
A
D
C
E
B
6G/5G
1G/5G
2G/10G
Drawback of fixed bandwidth-based route selection and related solution
Drawback of sequenced tunnel establishment and related solution
2
A
B
C
E
D
F
G
H
1
3
A
B
C
E
D
F
G
H
1
2
3
Tunnels are established in the following sequence: A-E > A-G > C-H. Tunnel C-H, however, fails to be established due to insufficient bandwidth.

## Slide 39: Network Traffic Optimization Overview
Network traffic optimization is to perform global analysis on network congestion, obtain the path computation result based on a proper optimization policy (ensuring the SLA of critical services), and apply the computation result to the network for congestion elimination.
Network traffic optimization can be divided into three phases: network information collection, path computation for network traffic optimization, and optimization result delivery.
1. Network information collection
The controller collects global network information, including:
Network topology
Network bandwidth
Link delay
Network traffic and other information
2. Path computation for network traffic optimization
The controller computes paths based on the optimization target. Optimization targets include:
Least path cost
Shortest path delay
Maximum link bandwidth utilization
...
3. Optimization result delivery
The controller delivers the computation result to network devices in any of the following modes:
NETCONF
PCEP
BGP SR Policy ...

## Slide 40: Network Information Collection
The collection of network information, including the network topology, interface bandwidth, link delay, and traffic statistics, is the prerequisite for network traffic optimization.
Collector, controller, and analyzer
SNMP
BGP-LS
PCEP
Telemetry
…
Network topology and interface bandwidth collection
In the industry, SNMP is generally used to collect basic network topology and device information.
BGP-LS is used to collect IGP and TE topology information (including interface bandwidth).
PCEP and BGP SR Policy are used to collect TE tunnel information.
Link delay collection
The link delay is collected using TWAMP, flooded in the IGP domain, and then reported to the controller through BGP-LS.
Traffic statistics collection
To determine bandwidth sufficiency and perform traffic optimization, the controller needs to collect interface and tunnel traffic statistics in real time.
Mainstream traffic statistics collection technologies include SNMP, telemetry, and NetStream.
Notes: Different collection protocols may be used in different solutions. For example, PCEP is used to collect TE tunnel information on Huawei MPLS networks, and BGP SR Policy is used to collect TE tunnel information on SRv6 networks.

## Slide 41: Network Optimization Computation
Network optimization computation refers to the computation of global or local optimal paths based on service requirements through the corresponding algorithms.
When computing paths, the controller needs to ensure that computed paths meet the related constraints. If the constraints cannot be met, the controller retains the original paths. The following table lists some constraints.
Constraint | Description
Priority | This constraint specifies the priorities of different types of tunnels and enables a tunnel with a higher priority to preempt the bandwidth resources of a tunnel with a lower priority.
Bandwidth | This constraint requires paths to be computed based on tunnel bandwidth requirements.
Hop count | This constraint requires paths to be computed based on hop count requirements. For example, the path length of an SR-TE tunnel is limited by the maximum stack depth (MSD) of the ingress node.
Explicit path | This constraint requires paths to be computed in either strict or loose mode. You can specify the links or nodes that are to be included or excluded.
Delay threshold | This constraint requires paths to be computed within the threshold range specified for path computation.
Affinity | This constraint supports the include-all, include-any, and exclude modes.
Least-cost path
Shortest-delay path
Bandwidth-balanced path
Maximum-availability path
Computation results
Meeting constraints
Notes: Bandwidth-balanced path: path with more remaining bandwidth among all paths that meet the constraints and have the same cost.
Maximum-availability path: path with the maximum availability among all paths that meet the constraints.

## Slide 42: Optimization Result Delivery
After the controller computes a network path, you can choose whether to apply the computation result to the network. There are multiple implementation modes:
Controller
NETCONF/YANG
PCEP
BGP SR Policy
Computation result delivery
1
NETCONF/YANG
The controller delivers the computation result to network devices as configurations.
The YANG model is standardized and provides good compatibility with different vendors.
2
PCEP
The controller delivers PCEP messages to create or update LSPs.
The PCEP standard does not define a tunnel model, and vendor-specific protocols cannot interoperate with each other.
3
BGP SR Policy
The controller uses BGP extensions to deliver tunnels.
The RFC defines the tunnel model and data packet structure in a unified manner, facilitating product interoperability between different vendors.

## Slide 43
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 44: New Requirements for Bearer Network SLA Assurance
An SLA is a formal commitment between a service provider and a customer. In the WAN service field, in addition to basic connectivity requirements, the SLA also focuses on deterministic delay, bandwidth, reliability, and isolation (security).
Generally, a bearer path carries the traffic of multiple types of services. When different types of service traffic are transmitted on the same path, differentiated bearer needs to be provided based on SLA requirements. Traditional QoS uses statistical multiplexing to set different priorities for specific services to ensure smooth experience of high-priority services. However, QoS falls short of meeting the isolation and deterministic delay requirements.
Network slicing can divide a bearer network into virtual networks of different service levels and provide dedicated logical channels for services with high quality and security requirements.
QoS requirements
Service requirements
Delay
Bandwidth
Jitter
Packet loss rate
Deterministic delay
Isolation
For example, fund settlement services between financial enterprises require high security and stable delay; the file transfer service within an enterprise requires high bandwidth; and enterprise voice services require low jitter.

## Slide 45: Slice-based Bearer Network: One Network for Multiple Purposes (Carrying Multiple Services), Lowering Costs
The IP network uses statistical multiplexing to greatly improve network utilization and reduce per-bit transmission costs. However, statistical multiplexing brings uncertainty to the quality assurance levels of different services. Moreover, it is inappropriate to prepare resources based on the highest SLA requirements to meet the requirements of all types of private lines and customers. The converged bearer network needs to balance multi-service isolation and statistical multiplexing to meet the SLA requirements of each service.
Slice resource reservation technologies, such as FlexE, channelized sub-interfaces, and QoS queues, can be used to direct services to respective service slices. These slices are isolated from each other and do not affect each other, providing different SLA levels.
Controller
Slice 1 (50 Mbit/s)
Slice 2 (50 ms)
Non-slice pipe (for common services)

## Slide 46: QoS Overview
QoS provides differentiated service quality for different applications.
Generally, QoS provides three service models: best-effort service, integrated service (IntServ), and differentiated service (DiffServ).
DiffServ is the most widely used QoS model on IP networks.
Three QoS service models
Best-effort service
IntServ
DiffServ
Applications can send any number of packets at any time.
The network tries its best to send packets and does not provide delay or reliability guarantee.
An application needs to apply for specific services before sending packets.
The network reserves network resources for the application using a protocol such as RSVP.
Traffic on the network is divided into multiple classes. A processing behavior is defined for each class, so that each class has a different forwarding priority, packet loss rate, and delay.
It is most widely used on IP networks.
QoS
FlexE
Channelized Sub-interface

## Slide 47: DiffServ Model-based QoS Components
DiffServ model-based QoS consists of four components: traffic classification and marking, traffic policing and shaping, congestion management, and congestion avoidance.
  Traffic classification and marking: Dividing data packets into different classes or configuring different priorities for packets is the prerequisite for implementing differentiated services. This component classifies data packets into different types, with each type of traffic being a traffic class. Traffic classification does not change the original data packets. In comparison, marking, which sets different priorities for data packets, changes the original data packets.
  Rate limiting (traffic policing and shaping): This component limits the rate of service traffic. It does this by discarding excess traffic when the service traffic exceeds the rate limit. Traffic policing controls the traffic receiving rate, and traffic shaping controls the traffic sending rate.
  Congestion management: This component buffers packets in queues upon network congestion and determines the forwarding order using a specific scheduling algorithm.
  Congestion avoidance: This component monitors network resource use. When congestion becomes severe, some packets are discarded to prevent network overload.
Traffic classification and marking is the prerequisite and foundation for implementing differentiated services.
Traffic policing, traffic shaping, congestion management, and congestion avoidance are used to control network traffic from different aspects.
QoS
FlexE
Channelized Sub-interface

## Slide 48: QoS Processing Sequence on Huawei Devices
QoS involves four major components: traffic classification and marking (behavior aggregate classification and multi-field classification), traffic rate limiting (CAR and traffic shaping), congestion management (queue scheduling), and congestion avoidance (drop policy). These four components work in a certain sequence on Huawei devices.
Receiving optical/electrical signals
Behavior aggregate classification
Interface card
Packet forwarding engine (PFE)
SFU
Uplink interface board
Service packets
Parsing packets
Multi-field classification
Searching the forwarding table
CAR
TM
Queue entering
Queue leaving
...
Scheuding
Queue entering: congestion avoidance
Queue leaving: traffic shaping
Receiving optical/electrical signals
Behavior aggregate classification
Interface card
PFE
Downlink interface board
Encapsulating packets
CAR
Multi-field classification
Obtaining encapsulation information
TM
Queue entering
Queue leaving
...
Scheuding
QoS
FlexE
Channelized Sub-interface
Notes: For the basic packet forwarding process, see HCIP-Datacom-Core Technology-01 Introduction to Network Devices.
Behavior aggregate classification: Packets are roughly classified based on the IP precedence or DSCP value of IP packets, TC value of IPv6 packets, EXP value of MPLS packets, and 802.1p value of VLAN packets to identify traffic with different priorities or service levels and implement internal-external priority mapping for the traffic.
Multi-field classification elaborately classifies packets based on complex rules, such as the 5-tuple (source address, source port number, protocol number, destination address, and destination port number).
Packet Forwarding Engine (PFE): After a router is powered on, it runs a routing protocol to learn the network topology and generate a routing table. If the interface board registers successfully, the main control board can generate forwarding entries according to the routing table and deliver entries to the interface board. In this manner, the router can forward packets according to the forwarding table. The component that forwards data packets is a chip located on an interface board and is called a packet forwarding engine (PFE).

## Slide 49
Notes: Traffic Management (TM): The interface board of a Huawei high-end router has a TM chip, which has a high-speed cache. In the case of congestion, data packets are temporarily stored in the cache in the form of queues. Then, the TM schedules the data packets out of the queue according to certain rules and sends the data packets to the switched network. If the cache capacity is exceeded, packets are discarded based on certain rules.
Committed access rate (CAR): The CAR ensures that the traffic does not exceed the bandwidth allowed by the inbound or outbound interface. Excess packets are directly discarded. Currently, CAR is used for traffic policing. CAR is implemented by the PFE. CAR can be implemented on the uplink PFE to ensure that the traffic rate does not exceed the bandwidth of the inbound interface. You can also perform CAR on the downlink PFE to ensure that the traffic rate does not exceed the bandwidth of the outbound interface.
Obtaining encapsulation information: On the downlink interface board, the obtained encapsulation information varies according to the forwarding technology. For example, the destination MAC address is obtained for IP forwarding, and the label information is obtained for MPLS forwarding.

## Slide 50: Behavior Aggregate Classification
Behavior aggregate classification allows a device to roughly classify packets based on simple rules.
802.1P
MPLS EXP
DSCP
Mapping
Service class
Color
Service class
Color
802.1p
MPLS EXP
DSCP
Mapping
SFU
Uplink direction
VLAN packets
MPLS packet
Behavior aggregate classification
Downlink direction
Different packets use different QoS priorities.
Packet header priority
Service class of a packet on the device
Service class
Internal drop priority of a packet on the device
Color
External priority
Internal priority
Drop priority
IP precedence
IP packet
QoS
FlexE
Channelized Sub-interface

## Slide 51: DSCP/IP Precedence/ 802.1p/EXP Value Mapping
802.1p | MPLS EXP | IP Precedence | DSCP | DSCP Name |  |  |  | 
7 | 7 | 7 | 56-63 | CS | CS7 |  |  | 
6 | 6 | 6 | 48-55 |  | CS6 |  |  | 
5 | 5 | 5 | 40-47 | EF | EF |  |  | 
4 | 4 | 4 | 32-39 | AF | AF4 | AF41 | AF42 | AF43
3 | 3 | 3 | 24-31 |  | AF3 | AF31 | AF32 | AF33
2 | 2 | 2 | 16-23 |  | AF2 | AF21 | AF22 | AF23
1 | 1 | 1 | 8-15 |  | AF1 | AF11 | AF12 | AF13
0 | 0 | 0 | 0-7 | BE | BE |  |  | 
Priorities in descending order
QoS
FlexE
Channelized Sub-interface

## Slide 52: Traffic Policing and Traffic Shaping
Both traffic policing and traffic shaping are traffic rate limiting technologies. The former monitors the incoming traffic of a device and limits the incoming traffic rate to a permitted range. If the traffic rate is too high, excess packets are discarded or the packet priorities are re-set. Traffic shaping controls the rate of outgoing packets, so that packets can be sent at an even rate.
Both traffic policing and traffic shaping use the token bucket algorithm to evaluate the traffic rate.
Traffic classification and marking
Queue 0
Queue 1
Queue 2
Queue N
...
Other processing...
Congestion avoidance
Entering queues
Scheduling
Congestion management
Traffic shaping
Leaving queues
Traffic policing
(CAR)
Incoming traffic
Outgoing traffic
Token
Token bucket
Token bucket technology
A token bucket evaluates traffic and determines whether packets meet forwarding conditions.
QoS
FlexE
Channelized Sub-interface

## Slide 53: Congestion Management and Congestion Avoidance
Queue 0
Queue 1
Queue 2
Queue N
...
Congestion avoidance
Entering queues
Scheduling
Congestion management
Traffic shaping
Leaving queues
Congestion management uses the queuing technology to handle network congestion. It buffers packets in different queues, groups the queues, and applies scheduling algorithms to process packets with different priorities.
Congestion avoidance is a flow control mechanism used to avoid queue congestion. It monitors the use of queues or memory buffers. When congestion occurs or aggravates, it discards packets newly entering queues to adjust the incoming traffic rate, alleviating network overload.
Traffic classification and marking
Other processing...
Traffic policing
(CAR)
Incoming traffic
Outgoing traffic
Incoming packet drop policy:
Tail drop
WRED
Queue scheduling algorithms:
First In First Out (FIFO)
Strict Priority (SP)
Weighted Fair Queuing (WFQ)
...
QoS
FlexE
Channelized Sub-interface
Notes: Weighted Random Early Detection (WRED): The system discards packets based on the drop policies configured for data packets or queues with different priorities. WRED is a congestion avoidance mechanism used to discard packets to prevent queues from being congested. For details, see the product documentation for Huawei NetEngine products.
FIFO: FIFO does not classify packets. FIFO allows packets to be queued and forwarded in the same order as they arrive at an interface.
SP: Queues are scheduled strictly according to their priorities. Packets in queues with a low priority can be scheduled only after all packets in queues with a higher priority are scheduled.
WFQ: The egress bandwidth is allocated to each flow according to the queue weight.
Other scheduling algorithms, such as RR polling, WRR weighted polling, and DRR differential polling, are not described here.

## Slide 54: Queue Group Scheduling Sequence
Each interface has eight queues, which are divided into three groups (PQ, WFQ, and LPQ). Scheduling algorithms can be applied to these queue groups respectively.
If PQ, WFQ, and LPQ queues use SP scheduling, PQ queues are scheduled first, then WFQ queues, and finally LPQ queues.
Start
Is the PQ queue empty?
Is the WFQ queue empty?
Is the LPQ queue empty?
Perform a round of PQ scheduling.
Perform a round of WFQ scheduling.
Perform a round of LPQ scheduling.
Yes
Yes
Yes
No
No
No
PQ queue
Queue 1
Queue m
...
WFQ queue
Queue 1
Queue i
...
LPQ queue
Queue 1
Queue k
...
WFQ
SP
SP
SP
Destination
interface
Port queue scheduling sequence
Queue scheduling process
QoS
FlexE
Channelized Sub-interface
Notes: PQ queue
  PQ queues use the SP scheduling algorithm. That is, the packets in the queue with the highest priority are scheduled first. In this way, an absolute priority can be provided for different service data, the delay of delay-sensitive applications such as VoIP can be guaranteed, and the use of bandwidth by high-priority services can be absolutely prioritized.
  Disadvantage: If the bandwidth of high-priority packets is not limited, low-priority packets may fail to obtain bandwidth and be scheduled.
  Generally, only delay-sensitive services enter PQ queues.
WFQ queue
  WFQ queues are scheduled based on weights. The WFQ scheduling algorithm can be used to allocate the remaining bandwidth based on weights.

## Slide 55
Notes: LPQ queue
  LPQ is a queue scheduling mechanism implemented on a high-speed link (Ethernet) interface. Low-speed links (such as serial and MP-Group links) do not support LPQ queues.
  Similar to PQ queues, SP scheduling is also used between LPQ queues. The difference lies in that PQ queues can preempt the bandwidth of WFQ queues in the case of congestion, whereas LPQ queues cannot do so. After PQ and WFQ queue scheduling is complete, the remaining bandwidth is allocated to LPQ queues.
  In actual applications, BE flows can be scheduled into LPQ queues. In this way, when the network load is heavy, BE flows can be completely contained to preferentially meet the requirements of other services.
All the eight queues on an interface can be configured as WFQ queues, PQ queues, LPQ queues, or a combination of WFQ and LPQ queues.

## Slide 56: WAN QoS Application: Flow Marking
WAN QoS is mainly applied to WAN links. A WAN link has much lower bandwidth than a local link and is often a congestion point for traffic forwarding. The purpose of deploying QoS on the WAN is to ensure the SLAs of different services.
It is recommended that CEs or the downstream devices of CEs mark DSCP priorities for service flows on the WAN. Then only behavior aggregate classification needs to be deployed on the VPN access interfaces of PEs.
WAN-P
WAN-P
WAN-P
Data center
Enterprise branch
Enterprise branch
BR-PE
BR-CE
BR-PE
BR-CE
City A
City C
City D
Data center
Data center
City B
The CE changes the DSCP values of different service flows to complete traffic classification.
Behavior aggregate classification is deployed on the VPN access interfaces of PEs for different services. Packets are mapped to queues based on DSCP values and then redirected to different tunnels on the WAN.
QoS
FlexE
Channelized Sub-interface
Notes: If the CE or the downstream device of the CE does not have the traffic marking capability, deploy multi-field classification on the ingress PE on the bearer WAN to mark traffic for queuing. This, however, affects the forwarding performance of the bearer WAN.

## Slide 57: WAN QoS Application: Flow Scheduling
The WAN's forwarding bottleneck lies in the egress WAN link in each region. For example, remote sites are interconnected through a carrier's MSTP private line, which has limited bandwidth. To prevent service flows from being discarded due to rate limiting after entering WAN links on the carrier network, deploy traffic shaping on egress WAN links to ensure that the traffic entering the carrier's MSTP private line does not exceed the rate limit.
Properly design QoS policies for enterprises' internal services. For example, deploy high-priority PQ scheduling for core production services or services with high QoS requirements and WFQ scheduling for services insensitive to packet loss and delay (only basic bandwidth for service continuity is needed in this case).
Service Type | Importance | Priority | Scheduling Mode
Protocol packet | High | CS7/CS6 | PQ
Core service | High | EF | PQ
Video service | High | AF4 | PQ
External service | High | AF3 | WFQ
Office and test services | Medium | AF2 | WFQ
Others | Low | BE | WFQ
QoS design for an enterprise
QoS
FlexE
Channelized Sub-interface

## Slide 58: QoS Limitations
QoS itself cannot solve the congestion problem or provide isolation and deterministic delay assurance for services:
  QoS involves only single-hop behaviors and does not change the network topology.
  QoS does not change service behaviors. If the bursty traffic of a single flow is too heavy, congestion still occurs.
  The number of QoS queues is small, and SLA assurance cannot be provided for specific users. As a result, deterministic delay assurance cannot be provided.
  The QoS mechanism is an experience system for resource management and cannot provide independent resources for users.
QoS is configured hop by hop. It cannot change forwarding paths, distinguish users, or provide independent resources.
QoS
FlexE
Channelized Sub-interface

## Slide 59: HQoS: Providing Scheduling and Bandwidth Guarantee for Users
On the basis of QoS, hierarchical quality of service (HQoS) provides finer-grained and more hierarchical scheduling and management of interface resources to implement fine-grained allocation and management of interface resources. Every scheduling queue can provide bandwidth guarantee, but the entire mechanism is based on QoS and cannot meet the deterministic delay and isolation requirements either.
QoS
Service scheduling
User scheduling
Service scheduling
HQoS
Multi-level service scheduling
Physical port
Dummy port queue (DQ)
Virtual interface (VI) queue
Group queue (GQ)
Subscriber queue (SQ)
Flow queue (FQ)
1
2
3
4
5
QoS
FlexE
Channelized Sub-interface

## Slide 60: HQoS: Providing User-Level Bandwidth Guarantee When the CIR of Each Scheduler Does Not Exceed the Upper Limit
HQoS adds hierarchical schedulers such as SQ, GQ, and VI. Each scheduler has two attributes (CIR and PIR) and uses SP scheduling for flows whose rates are between the CIR and PIR. The CIR is preferentially guaranteed.
HQoS guarantees bandwidth through strict CIR deduction and shaping. The sum of the CIRs of all schedulers is less than the interface bandwidth.
802.1p
DSCP
Queue CS7
Queue CS6
Queue EF
Queue AF4
Queue AF3
Queue AF2
Queue AF1
Queue BE
Queue CS7
Queue AF4
Queue BE
Queue CS7
Queue AF4
Queue BE
Shaping
Shaping
Shaping
802.1p
DSCP
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
Shaping
802.1p
DSCP
SQ1
SQ2
SQ3
SQ4
DWRR
DWRR
GQ1
GQ2
DWRR
VI
VI
DWRR
DP
QoS
FlexE
Channelized Sub-interface

## Slide 61: Channelized Sub-interfaces Providing Management Entities on the Basis of HQoS to Provide SLA Assurance
Bandwidth guarantee: Channelized sub-interfaces use HQoS-based hierarchical scheduling to implement flexible and refined resource management. Each channelized scheduling tree has independent buffer resources and bandwidth resources, providing bandwidth guarantee.
Delay guarantee: Because the resources for channelized sub-interface are strictly guaranteed, the delay can be guaranteed within a certain range.
Channelized sub-interfaces use the HQoS mechanism and exclusively occupy the HQoS VI/GQ scheduling trees and bandwidth to implement strict scheduling isolation.
Remaining bandwidth of a main interface = Total interface bandwidth – Total bandwidth of all channelized sub-interfaces. Bandwidth is automatically deducted during the channelized sub-interface enabling process, simplifying the HQoS application model.
Channelized sub-interfaces provide management entities and can work with the controller for resource management and E2E resource reservation, meeting the SLA assurance requirements of P2MP services.
FQ 1-8
SQ
GQ/VI
Scheduling tree of a channelized sub-interface
200M
DP
FQ 1-8
SQ
GQ/VI
Default scheduling tree of a main interface
1000M – 200M = 800M
Each channelized sub-interface exclusively occupies a VI/GQ queue.
WRR
1000 M
QoS
FlexE
Channelized Sub-interface

## Slide 62: FlexE: Delivering Isolation and Deterministic Delay Assurance Based on Independent Resources
Flexible Ethernet (FlexE) is a new technology introduced between the MAC and PHY layers. It is a lightweight enhanced technology for IP networks and is compatible with the existing Ethernet standard and QoS capabilities.
It provides isolated FlexE interface links, enabling one network to carry different types of services.
It provides an independent P2P time division multiplexing (TDM) tunnel for each service, meeting isolation and deterministic delay requirements.
Low delay
TDM switching
High bandwidth
Statistical multiplexing
10G
80G
Deterministic delay
Statistical multiplexing
10G
MAC
PHY
IP
QoS scheduling
FlexE
PHY
MAC
IP
QoS scheduling
Statistical multiplexing
PHY
100G
PHY
100G
QoS
FlexE
QoS
FlexE
Channelized Sub-interface

## Slide 63: Basic FlexE Architecture
FlexE decouples the MAC layer from the PHY layer by introducing the FlexE shim layer on the basis of IEEE 802.3, thereby providing flexible rates.
FlexE adopts the client/group architecture and allows client interfaces at different rates to coexist in a FlexE group.
Client: corresponds to various user interfaces on a network. Each FlexE client can flexibly apply for bandwidth from the resource pool of a FlexE group, adjust the bandwidth, and transfer data flows to the FlexE shim layer as 64B-/66B encoded bit streams.
Group: consists of various Ethernet PHY layers defined in IEEE 802.3 and divides the PHY bandwidth into 1G timeslots (supported by Huawei devices) or 5G timeslots.
Shim: an extra logical layer inserted between the MAC and PHY layers of the traditional Ethernet architecture. It implements key FlexE functions through calendar timeslot distribution.
FlexE shim
FlexE shim
FlexE client
FlexE client
FlexE group
QoS
FlexE
Channelized Sub-interface

## Slide 64: Comparison of Slicing Technologies
QoS: All traffic shares eight queues. QoS schedules resources in a unified manner to maximize the statistical multiplexing capability. It cannot differentiate users, and so cannot provide independent resource reservation for different users.
FlexE: Queue and interface resources are isolated. Every resource is divided by TDM timeslot. This meets the requirements for exclusive resource use and resource isolation and provides flexible and refined management of interface resources.
Channelized sub-interface: Queue resources are isolated. Hierarchical scheduling is used to implement flexible and refined management of interface resources, provide bandwidth guarantee, and work with the controller to provide E2E resource reservation.
DP
SQ
GQ
VI
MAC
PHY
TM
PIC
CS7
BE
SQ
GQ
VI
TM
PIC
Channelized sub-interface
DP
MAC
PHY
CS7
BE
SQ
GQ
VI
CS7
BE
Channelized sub-interface
...
TM
PIC
...
SQ
DP
FlexE client
FlexE shim
PHY
CS7
BE
FlexE client
SQ
DP
CS7
BE
MAC

## Slide 65: Slicing Technology Implementation Modes
Interface Name | Usage Scenario and Feature Description
FlexE sub-interface (also called client interface) | A physical interface in standard Ethernet mode has fixed bandwidth. FlexE, however, can enable one or more physical interfaces to work in FlexE mode and add them to a group. The total bandwidth of this group can be allocated on demand to logical interfaces in the group. The group to which physical interfaces are added is referred to as a FlexE group. The logical interfaces that share bandwidth of the physical interfaces in the FlexE group are called FlexE interfaces (also referred to as FlexE service interfaces). FlexE interface bandwidth varies, which allows services to be isolated. Compared with traditional technologies, FlexE technology permits bit-level interface bundling, which solves uneven per-flow or per-packet hashing that challenges traditional trunk technology. In addition, each FlexE interface has a specific MAC address, and forwarding resources between interfaces are isolated. This prevents head-of-line (HOL) blocking that occurs when traditional logical interfaces such as VLAN sub-interfaces are used for forwarding. FlexE interface technology especially fits scenarios in which high-performance interfaces are required for converged bearer, such as mobile bearer, home broadband, and private line access. Services of different types are carried on different FlexE interfaces and are assigned bandwidth based on FlexE interfaces. In this way, FlexE achieves service-specific bandwidth control, meeting network slicing requirements in 5G scenarios.
VLAN channelized sub-interface | A channelized interface can strictly isolate interface bandwidth. A VLAN channelized sub-interface is a channelization-enabled sub-interface of an Ethernet physical interface. Different types of services are carried on different channelized sub-interfaces and assigned bandwidth based on channelized sub-interfaces. This implementation strictly isolates bandwidth among different channelized sub-interfaces on the same physical interface and achieves service-specific bandwidth control, preventing bandwidth preemption among different sub-interfaces.
Ethernet sub-interfaces | An Ethernet sub-interface is a virtual interface configured on a main interface and has Layer 3 features. You can configure an IP address for an Ethernet sub-interface to implement inter-VLAN communication. The main interface can be either a physical interface or a logical interface. The sub-interface inherits the physical layer parameters of the main interface but has its own link layer and network layer parameters. You can activate or deactivate the sub-interface, without affecting the performance of the main interface. The change of the main interface status, however, affects the sub-interface.

## Slide 66: Network Slicing Solution Example: SRv6 & Slice ID
Control plane
Simplified configuration
  Leveraging the existing SRv6 network, slices do not require IP address configuration.
  During slice deployment, IGP/BGP configurations do not need to be modified, exerting little impact on the live network.
Elastic scaling
  Support for 1000+ network slices
  Support for bearer of slices over SRv6 Policies in loose explicit path mode
VLAN
VLAN
VLAN
Physical main interface
Default slice
Service slice
Service slice
Slice service 1
Slice service 2
Slice service 3
VLAN
VLAN
VLAN
SliceID1
Slice ID2
Slice ID3
+
SRH
IPv6 Header
=
Slice tunnel 1
Slice tunnel 2
Slice tunnel 3
ETH
VLAN
IP Header
Payload
SRv6 BE
SRv6 Policy
ETH
VLAN
IP Header
GTP
Payload
ETH
IPv6 Header (VPN SID)
HBH SliceID
IP Head
Payload
ETH
IPv6 Header
HBH Slice ID
SRH
IP Header
Payload
Slice ID description
  Globally unique network slice identifier.
  Corresponding to all forwarding resources on the slice plane
  Slice ID carried in packets on the forwarding plane end to end
  Each forwarding node matching a set of slice forwarding resources based on the corresponding slice ID hop by hop
ETH
IPv6 Header (VPN SID)
HBH SliceID
IP Header
Payload
ETH
IPv6 Header
HBH Slice ID
SRH
IP Header
Payload
Slice service 1
Slice service 2
Slice service 3
Forwarding plane
VRF1
VRF2
VRF3
VRF1
VRF2
VRF3
Notes: Different VLANs are used for service access. Logical interfaces correspond to VPN instances VRF1, VRF2, VR3... on the network slice.
The ingress PE encapsulates the VPN SID and SRv6 Policy information into the service flow on the network slice with the slice ID being 2, and inserts an extension header with the Hop By Hop Slice ID being 2 between the IPv6 header and SRH of each packet.
Each transit node queries the SRv6 SID in the SRH hop by hop to obtain the physical outbound interface, and then queries the specific "resource reservation" sub-interface of the physical outbound interface based on the slice ID. The Hop By Hop Slice ID remains unchanged throughout this process.
The egress PE pops the Hop By Hop extension header and forwards the packet to the AC interface of the corresponding VPN instance based on the VPN SID.
By default, the slice ID is 0, and the IPv6 Hop By Hop extension header does not need to be inserted. The packet format on the forwarding plane is the same as that of traditional L3VPN over SRv6 Policy.

## Slide 67
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 68: WAN Reliability Overview
WAN reliability covers two parts: device reliability and network reliability.
Device reliability: includes router reliability and controller reliability.
  Controller reliability is implemented through cluster deployment and disaster recovery (DR) system deployment.
  Router reliability can be implemented using device features such as non-stop routing (NSR). These features are beyond the scope of this course.
Network reliability: reduces the impact of link and node faults on services through fast detection and convergence mechanisms at each layer.
Notes: Because different WAN VPN technologies use different terms, this section briefly describes various protection mechanisms, but does not describe specific protection technologies.

## Slide 69: TE Tunnel Protection Technology Basics
MPLS TE tunnel protection can be provided from two perspectives: local protection and E2E protection. TE tunnels, including MPLS TE tunnels, SR-MPLS TE tunnels, and SR-MPLS Policies can all be protected from the two perspectives, but their technical implementation is slightly different.
E2E protection
E2E protection: establishes multiple CR-LSPs between the ingress and egress of a tunnel, with each CR-LSP traversing a different path. When detecting that the primary CR-LSP is faulty, the ingress switches traffic to the backup CR-LSP.
In E2E protection, path switching is slow. Therefore, E2E protection needs to be used with a detection mechanism for fast path switching.
Local protection
Fast reroute (FRR), also called local protection, is a temporary protection measure. If a transit node/link fails, local protection is triggered. A backup CR-LSP is then established locally for traffic switching. In addition, the tunnel ingress is instructed to recompute a path and switch traffic to the backup path in a timely manner.
R2
R1
Path 1: primary path
Path 2: backup path
MPLS TE tunnel
Primary CR-LSP
Local backup CR-LSP
Configuring FRR
Triggering local protection
Notes: MPLS TE E2E protection is classified into HSB and ordinary backup. In HSB protection, the backup path and primary path are created at the same time.
Segment Routing adopts Topology Independent-Loop Free Alternate (TI-LFA), an enhancement of FRR, for local protection.
Fast detection mechanism: Fast detection mechanisms represented by BFD support fast detection of communication faults between devices.

## Slide 70: TI-LFA FRR
TI-LFA FRR provides link and node protection for SR tunnels. If a link or node fails, traffic is rapidly switched to the backup path.
Limitations of the traditional LFA algorithm
R1
R2
R3
R4
SIP: 1.1.1.1
DIP: 4.4.4.4
Cost=10
Cost=10
Cost =10
Cost =100
The traditional LFA algorithm has topological limitations. As shown in the figure, SIP traffic is forwarded to the DIP through R1. If the R1-R3 link fails, R1 forwards the traffic to R2. However, no backup path can be formed before R2 detects the failure.
TI-LFA algorithm
R1
R2
R3
R4
SIP: 1.1.1.1
DIP: 4.4.4.4
Cost=10
Cost=10
Cost =10
Cost =100
Using the source routing capability of SR, TI-LFA computes a backup path on each node to protect the failure point. When a node detects a failure, traffic is rapidly switched to the backup path.
Primary R1-R3 path: 4.4.4.4; segment list: R1, R3
Backup R1-R3 path: 4.4.4.4; segment list: R1, R2, R4, R3
Notes: In a distributed network architecture, each device independently calculates paths, and there is no consensus on the shortest path when a fault occurs. As a result, traditional LFA cannot form a backup path.

## Slide 71: Limitations of E2E Protection
Technologies such as HSB can protect E2E paths, but cannot rectify faults on PEs.
In this example, a TE tunnel with both primary and backup paths is established between PE1 and PE2. If PE2 is faulty, the backup path cannot solve the problem.
PE1
P1
P3
P4
P2
PE2
PE3
CE1
CE2
Primary path
Backup path
MPLS TE tunnel

## Slide 72: VPN FRR
VPN FRR sets the primary and backup forwarding paths pointing to the active and standby PEs on the remote PE in advance. It works with fast PE fault detection to accelerate fault-triggered E2E service convergence in scenarios where a CE is dual-homed to two PEs.
PE1
P1
P3
P4
P2
PE2
PE3
CE1
CE2
Backup path of tunnel 1
Primary path of tunnel 1
VPN FRR backup path (primary path of tunnel 2)
Tunnel 1
Primary path of tunnel 1
Backup path of tunnel 1
Tunnel 2
Primary path of tunnel 2

## Slide 73: IP FRR
If the link between PE2 and CE2 fails but PE2 still functions properly, the tunnel between PE1 and PE2 is still available. In this case, E2E tunnel switching is not required. PE2 selects PE3 as the backup next hop. If the link between PE2 and CE2 or CE2 fails, IP FRR is implemented to rapidly switch IP traffic.
IP FRR is applicable to the IP network between CEs and PEs.
PE1
P1
P3
P4
P2
PE2
PE3
CE1
CE2
Primary path of tunnel 1
Tunnel 1
Primary path of tunnel 1
Backup path of tunnel 1
Tunnel 2
Primary path of tunnel 2
CE3
IP FRR

## Slide 74: Summary: Multi-Level Network Protection
To sum up, different protection measures are taken to ensure tunnel reliability based on the locations of faults on E2E paths.
From the perspective of E2E forwarding paths, it is recommended that multi-level protection be used:
Protection against faults on the intermediate links and nodes of tunnels
Tunnel egress protection
PE2
P1
P3
P4
P2
PE3
PE4
CE1
CE2
CE3
E2E path
Protection against remote CE faults
Protection against CE access faults
PE1

## Slide 75
Bearer WAN Architecture
Bearer WAN Basics
VPN Service
Network Traffic Optimization
SLA
Network Reliability
Network Management and O&M

## Slide 76: WAN Management and O&M
Among mainstream WAN solutions provided by different vendors, the SDN solution is preferred. The SDN controller centrally manages and delivers WAN services to forwarders.
In Huawei's solution, the controller not only provides "control" functions, but also provides "management" and "analysis" functions.
NETCONF
Telemetry, SNMP, BGP-LS
Ingress
Egress
Transit
Transit
TWAMP
iFIT
(Management+control+analysis)
Network measurement
Network collection/management
Network analysis
Network performance indicators, such as the delay, jitter, and packet loss rate, are measured.
The AI algorithm is used to obtain network analysis results based on massive amounts of network performance and monitoring data.
Multiple protocols and channels are used to collect network configuration data, performance data, and monitoring data.
Efficient network configuration management is provided.
Notes: This figure does not show protocols related to tunneling and traffic statistics collection.

## Slide 77: SNMP
Simple Network Management Protocol (SNMP) is a network management standard widely used on TCP/IP networks.
It provides a method for managing devices through a central computer that runs network management software — known as a network management station (NMS).
By employing the "network management over networks" mode, SNMP implements efficient and batch network device management. In addition, SNMP enables unified management of network devices of different types and from different vendors.
SNMP overview
SNMP
NMS (SNMP server)
e.g.: iMaster NCE
Managed device (SNMP client)
e.g.: router, switch...
Agent process
MIB

## Slide 78: NETCONF
SNMP is not a configuration-oriented protocol. On a large-sized network with a complex topology, SNMP cannot meet network management requirements, especially the configuration management requirements.
SNMP's drawbacks
NETCONF
NMS (NETCONF client)
e.g.: iMaster NCE
The Network Configuration Protocol (NETCONF) provides a mechanism for the NMS to communicate with network devices.
To be specific, the network administrator can use this mechanism to add, modify, and delete the configurations of network devices as well as obtain the configurations and status of network devices.
NETCONF uses a YANG file to describe the data model of a device. A YANG file has a more hierarchical structure than a MIB file.
NETCONF overview
Data model
Managed device
(NETCONF server)
YANG

## Slide 79: Telemetry
Telemetry, also known as network telemetry, is mainly used to monitor networks, including packet check and analysis, intrusion and attack detection, intelligent data collection, and application performance management. Generally, it is used together with NETCONF. The analyzer analyzes the data collected by telemetry and then instructs the controller to automatically modify device configurations based on analysis results.
Advantages of telemetry:
  Is developed based on the YANG model.
  Collects a wide variety of data with high precision to fully reflect network status.
  Continuously reports data with only one-time data subscription.
  Locates faults rapidly and accurately.
Collector
Controller
Analyzer
Telemetry-based data uploading
NETCONF-based configuration delivery
Network device
Subseconds
YANG model

## Slide 80: BGP-LS
BGP-LS introduces new NLRI into BGP. The NLRI carries link, node, topology prefix, and other information, and is also referred to as the link state NLRI.
BGP-LS can aggregate network-layer topology, bandwidth, delay, and other information and send the information to the controller for path computation.
BGP-LS
(topology, bandwidth, delay)
Controller
BGP-LS
IGP
TWAMP
TE
SR
BGP-LS aggregates information collected by various network layer protocols, including:
  IGP: IGP information of each AS
  TWAMP: measurement information, such as interface delay
  TE: TE information, such as bandwidth
  SR: SR information, such as SR labels

## Slide 81: TWAMP
Two-Way Active Measurement Protocol (TWAMP) measures the two-way delay, jitter, and packet loss rate between devices on an IP network. It performs negotiation over a TCP connection and uses UDP data packets as measurement packets.
Session-Sender
Session-Reflector
Control-Client
Server
Control
Test
TWAMP communication model
Control-Client: establishes, starts, and stops a test session and also collects statistics.
Server: responds to the Control-Client's request for establishing, starting, or stopping a test session
Session-Sender: proactively sends probes for performance statistics after being notified by the Control-Client.
Session-Reflector: replies to the probes sent by the Session-Sender with response probes after being notified by the Server.
Test plane
Control plane
Notes: TWAMP Light is a lightweight version of TWAMP defined based on standard protocols. Compared with TWAMP, TWAMP Light simplifies the control protocol used to establish performance measurement sessions.

## Slide 82: TWAMP Light
As the light version of TWAMP, TWAMP Light eliminates the necessity of the TWAMP-Control protocol, and moves the control plane from the Responder to the Controller so that TWAMP control modules can be centrally deployed on the Controller. Therefore, TWAMP Light greatly relaxes its requirements on the Responder performance, allowing the Responder to be rapidly deployed.
The Control-Client, Server, and Session-Sender are deployed on the same host and function as the Controller. Therefore, the control session establishment process in the standard architecture can be ignored in the performance detection process. The Session-Reflector is deployed on another host as the Responder.
Server
Control-Client
Session-Sender
Session-Reflector
The Controller sends test packets to the Responder, and the Responder functions as the Session-Reflector to reflect the test packets.
The Session-Reflector does not need to learn Session status. After receiving the test packets, the Session-Reflector copies the necessary information, generates a test packet sequence number and timestamp, and returns the test packets to the Controller.
Upon receiving the reflected test packets, the Controller collects the indicators in both path directions.
Controller
Responder
TWAMP test
No control plane negotiation
Notes: The standard TWAMP version uses TCP for control plane negotiation, and test packets are based on UDP. The reflector needs to know the session status so that devices of different vendors can communicate with each other.
TWAMP Light does not involve control plane negotiation, and test packets are also based on UDP. The implementation and configuration are simple, and the reflector does not need to know the session status.

## Slide 83: TWAMP Application Scenarios
With TWAMP, NEs do not need to generate or maintain IP network performance statistics. The performance management system can easily obtain statistics about the entire network by managing only the TWAMP clients initiating statistics collection requests. In this way, IP performance statistics are collected quickly and flexibly.
TWAMP is used on enterprise WANs to measure the delay, jitter, and packet loss rate between any two nodes, providing a reference for troubleshooting and traffic optimization.
The Controller instructs network devices to establish performance measurement sessions. For example, R1 functions as the Control-Client to initiate IP performance measurement.
R1 and R2 initiate a TWAMP measurement session.
R1 reports the measurement result to the Controller.
R1
R2
Performance management system
1
3
2

## Slide 84: iFIT
Traditional out-of-band measurement principles (ping, traceroute, TWAMP...)
Ingress
Egress
Actual traffic path
Test packet path
Traditional out-of-band measurement principles (Y.1731, Y.1711...)
Test packets are not actual service data and may be transmitted along different paths.
Ingress
Egress
Sampled packets
Only pipe-based detection is available. Service-level detection is not supported.
Packets are sent at intervals, and the sampling precision is low.
iFIT
Per-flow: Service packets are checked to reflect the actual service path and delay information.
Per-packet: Packets are checked one by one, accurately reflecting service packet loss.
Controller
Telemetry
1
1
1
0
0
0
Coloring period T1
T2
Timestamp t1
1
1
1
0
0
Coloring period T1
T2
Timestamp t2
Link delay = Receiving time of the local node – Sending time of the upstream node
Packet loss location: Telemetry reports information about each node and compares the information to obtain the packet loss location.
Segment KPI
Segment KPI
Segment KPI
E2E KPI
Notes: iFIT measures E2E service packets to obtain performance indicators of an IP network, such as the packet loss rate and delay. iFIT adds a color flag to the packet header in the service flow. Telemetry is used to periodically collect information. Features such as E2E delay measurement and packet loss measurement are supported.

## Slide 85: iFIT for VPN over SRv6 Scenario
Basic SRv6 scenario:
  The ingress inserts the SRH between the IPv6 header and payload. The SRH carries the SRH basic header and iFIT extension header.
  SRv6-capable nodes can report iFIT statistics in either E2E or hop-by-hop mode.
  A node that does not support SRv6 but supports IPv6 forwarding can properly forward service packets carrying iFIT information.
PE1
P1
P3
PE2
NCE-IP
ETH
Payload
Telemetry
VRF 100
END.DT4 SID: B::1:1:D100
DA: B::1:1:D100
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
DA: B::1:1:D100
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
DA: B::1:1:D100
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
ETH
Payload
Notes: An End.DT4 SID (PE endpoint SID) identifies an IPv4 VPN instance on a network.
For MPLS packets, the iFIT header is inserted between the MPLS label and MPLS payload.

## Slide 86: iFIT for SRv6 Policy Scenarios
In an SRv6 Policy scenario:
  The iFIT extension header is encapsulated into the Optional TLV field of the SRH.
  SRv6-capable nodes can report iFIT statistics in either E2E or hop-by-hop mode.
  A node that does not support SRv6 but supports IPv6 forwarding can properly forward service packets carrying iFIT information.
DA: P1
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
(PE2,P3,P1)SL=2
DA: P3
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
(PE2,P3,P1)SL=1
DA: PE2
SRH basic header
iFIT (E2E/Trace)
Payload
ETH
(PE2,P3,P1)SL=0
PE1
P1
P3
PE2
NCE-IP
Telemetry
VRF 100
END.DT4 SID: B::1:1:D100
ETH
Payload
ETH
Payload

## Slide 87: iFIT-based Service Path Display
In each measurement period, a device reports the flow direction, interface number, and TTL information when reporting packet statistics.
iMaster NCE-IP restores the path information of the flow based on the information reported by each node.
The implementation is independent of the tunnel type (SRv6/SRv6 Policy/SR-MPLS TE/SR-MPLS BE/MPLS...).
Path restoration
R3
R2
R5
R4
R6
R1
GE 1/0/0
GE 1/0/2
GE 1/0/0
GE 1/0/2
GE 1/0/0
GE 1/0/2
GE 1/0/0
GE 1/0/2
TTL=255
TTL=254
TTL=253
TTL=252
iMaster NCE-IP

## Slide 88: iFIT-based Fault Locating
Path aggregation is performed based on the physical topology, end nodes of poor-QoE services, and the built-in AI algorithm of iMaster NCE-IP to determine the minimum area that causes poor service quality, helping further locate and demarcate faults.
iFIT
R3
R2
R5
R4
R6
R1
iMsater NCE-IP
Service 1
Service 2
Service 3
Find out poor-QoE services, such as services 1 to 3, on the entire network.
Intelligently compute the common paths of the three services.
Select a service for iFIT-based fault detection. Service 1 is used as an example here.
Determine the faulty device R5 based on per-hop iFIT measurement.
R1
R3
R5
R6
iMaster NCE-IP
Service 1

## Slide 89
(True or False) An SR Policy is identified by <headend, color, endpoint> and contains multiple candidate paths. ( )
  True
  False
(Multiple-answer question) Which of the following are WAN bearer technologies? ( )
  SR-MPLS
  SRv6
  MPLS LDP
  MPLS TE
Notes: A
ABCD

## Slide 90
This course introduces the concepts and principles of the enterprise bearer WAN's typical architecture, bearer technologies, VPN services, traffic optimization, SLA, reliability, and network management and analysis. To introduce these key aspects, this course uses a large enterprise with three data centers in two cities and multiple branches in different regions as an example.
On a real production network, engineers need to determine the network architecture and technical applications based on the live network conditions and enterprises' services.