## Slide 1
Datacom
V5R2
V1.0
He Junjian/WX580230
2021.02.25
Wan Changli/WX408647
New

## Slide 2: WAN VPN Technologies

## Slide 3
A virtual private network (VPN) is established using the WAN IP technology. A VPN, as its name suggests, has two features: virtual and private. Different VPNs share the underlying bearer network while logically isolating services.
Before Segment Routing IPv6 (SRv6) came into place, a WAN VPN was generally carried over an MPLS network. And a WAN VPN carried over an MPLS network is called an MPLS VPN.
This course introduces the models and classification of WAN VPN technologies, followed by the architecture fundamentals and evolution of these technologies.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the models and classification of WAN VPN technologies.
  Describe the relationships between MP-BGP and WAN VPNs.
  Describe the fundamentals of MPLS VPNs and SRv6 VPNs as well as differences between the two types of VPNs.
  Describe the development trend of WAN VPN technologies.

## Slide 5
WAN VPN Overview
MP-BGP Overview
WAN VPN Architecture Fundamentals and Technology Evolution

## Slide 6: WAN VPN Overview
A virtual private network (VPN) is established using the WAN IP technology. A VPN, as its name suggests, has two features: virtual and private. Different VPNs share the underlying bearer network while logically isolating services.
Enterprise branch
Data center
Enterprise HQ
IP bearer WAN
VPN
Private
A VPN is a network dedicated to VPN users. For VPN users, a VPN provides the same service experience as a traditional private network. A VPN provides security assurance to protect VPN information against external threats. Different VPN services can be carried over the same underlying network while being isolated from each other.
Virtual
VPNs provide logical private networks over the same public physical bearer network through the virtualization technology. You can create multiple logical private networks based on service requirements.
Tunnel
Tunnel
Tunnel
Data center
MPLS LDP/SR-MPLS/SRv6
Notes: In HCIP-Datacom-Core Technology > VPN Technology Overview, we learned that VPNs can be built over the Internet (e.g. IPsec VPN, L2TP VPN, SSL VPN, etc.) or private networks (MPLS VPN). In this course, we will learn the development and evolution of WAN VPN technologies.

## Slide 7: Development of WAN IP Technologies
WAN technologies are evolving towards all IP. For example, IP/MPLS replaces asynchronous transfer mode (ATM), and IEC 61850 enables IP-based power communication networks. WAN IP technologies are widely used in enterprise scenarios, such as power/transportation bearer networks, financial DCI networks, ISP backbone networks, and metro networks.
WAN IP technologies are evolving from classic IP/MPLS to SR-MPLS and even SRv6.
Enterprise campus
3. Power/ transportation bearer network
1. ISP backbone network
2. ISP metro network
Egress router
Data center
Campus
WAN
Enterprise branch
Home
Data center
Data center
4. DCI
IP/MPLS
SR-MPLS
SRv6

## Slide 8: Basic WAN VPN Model
A WAN VPN consists of three device roles: customer edge (CE), provider edge (PE), and provider (P).
CE
CE
P
PE
PE
PE
VPN site 1
P
CE
CE
Backbone network
VPN site 2
VPN site 1
VPN site 2
P
P
Notes: CE: user-side edge device that connects to service provider devices. A CE connects to one or more PEs for user access.
PE: service provider edge device connecting to the CE. PEs are important network nodes that connect to both CEs and Ps.
P: service provider device that does not connect to any CE.

## Slide 9: Classification of Traditional WAN VPNs
Depending on service types and network characteristics, VPNs are classified into L3VPNs and L2VPNs:
  L3VPNs: carry Layer 3 services. L3VPNs use VPN instances to isolate services.
  L2VPNs: carry Layer 2 services. L2VPNs use pseudo wires (PWs) to isolate services. Typical L2VPNs are VPWSs and VPLSs.
PE
Service 1
Service 1
MPLS LDP
SR-MPLS/SRv6
10.1.1.1/24
IP bearer WAN
PE
Service 2
L3VPN
L2VPN
20.1.1.1/24
Service 2
10.1.1.1/24
10.1.1.2/24
Notes: As networks are moving towards all IP, most network services are Layer 3 IP services, and most VPNs are deployed as L3VPNs.
Traditional L2VPN services include VPLS services and VPWS services. The VPLS service is a multipoint-to-multipoint L2VPN service, and the VPWS service is a point-to-point L2VPN service.

## Slide 10: WAN VPN Classification Based on IP Bearer Technologies
Depending on IP bearer technologies, WAN VPNs can be classified into MPLS VPNs and SRv6 VPNs.
L3VPN
L2VPN
MPLS/IP
MPLS VPN
The underlying bearer network of MPLS VPNs uses MPLS/IP on the forwarding plane. MPLS can carry L2VPN and L3VPN services.
L3VPN
L2VPN
IPv6
SRv6 VPN
The underlying bearer network of SRv6 VPNs uses IPv6 on the forwarding plane.
SRv6 is a segment routing technology that uses IPv6 addresses as segments and is widely considered as the evolution direction of next-generation WANs.

## Slide 11: Hierarchical WAN VPN Technology Architecture
The WAN VPN technology architecture can be simply divided into two planes: data plane and control plane.
The control plane is responsible for transmitting CE-side route information, and the data plane is responsible for forwarding packets.
WAN
P
PE2
PE1
CE1
192.168.1.0/24
Site A of user X
192.168.2.0/24
CE3
192.168.2.0/24
Site B of user X
192.168.1.0/24
Bidirectional route transmission
Bidirectional packet forwarding
Control plane
Data plane

## Slide 12: Overview of WAN VPN Technologies
In the course of development, IP technologies are constantly evolving. There are multiple types of WAN VPN control and data plane technologies, and these technologies can be flexibly combined to meet the requirements of different service scenarios.
  The control plane uses MP-BGP, which supports the use of different address families to transmit different route information.
  The WAN data plane mainly uses MPLS/IP, SR-MPLS, or SRv6.
Control plane (MP-BGP)
Data plane
L3VPNv4
L2VPN
MPLS/IP
SR-MPLS
SRv6
L3VPNv6
EVPN
Notes: L2VPN in the figure refers to the BGP L2VPN-AD address family on the Huawei device. It is used to exchange VPLS/VPWS information between MP-BGP peers.
More data plane tunneling technologies, such as GRE, IPsec, and VXLAN, are used in other scenarios such as SD-WAN and DCN and are not described here.

## Slide 13
WAN VPN Overview
MP-BGP Overview
WAN VPN Architecture Fundamentals and Technology Evolution

## Slide 14: MP-BGP Overview
Multiprotocol Extensions for BGP-4 (MP-BGP), defined in RFC 4760, is used to extend BGP-4 to enable BGP to carry route information for multiple network layer protocols, such as IPv6, L3VPN, and EVPN.
The extensions are backward compatible. That is, a router that supports MP-BGP can exchange route information with a router that supports only BGP-4.
IPv4
EVPN
L3VPN
IPv6
IPv4
BGP speaker
BGP speaker
BGP speaker
R1
R2
R3
BGP-4
MP-BGP
Notes: https://datatracker.ietf.org/doc/rfc4760/

## Slide 15: Example: BGP-4 Update Message
BGP-4 has three attributes specific to the IPv4 address family: NEXT_HOP, AGGREGATOR, and IPv4 NLRI.
On the network shown in the figure, R1 sends a BGP-4 Update message to R2. The advertised network segment is 10.0.0.0/8, and the next hop address is 1.1.1.1.
In a BGP Update message, the NLRI field carries IPv4 network segment information, and the NEXT_HOP attribute in the Path attributes field carries the next hop address.
BGP-4 Update message
Path attributes
NEXT_HOP: 1.1.1.1
NLRI (IPv4)
10.0.0.0/8
R1
1.1.1.1/32
R2
R3
3.3.3.3/32
10.0.0.0/8
BGP-4
MP-BGP

## Slide 16: Example: MP-BGP Update Message
To enable MP-BGP to support new address families and provide compatibility with IPv4, the IETF adds two more path attributes: MP_REACH_NLRI and MP_UNREACH_NLRI. The former indicates reachable destination information, and the latter indicates unreachable destination information.
The structures of MP-BGP and BGP-4 Update messages are slightly different. On the network shown in the figure, R3 advertises the following VPNv4 route information to R2. The RD and IPv4 route information is stored in the new NLRI field, and the RT is stored in the community attribute of the Path attributes field.
MP-BGP Update message
Path attributes
Extended community 10:10
MP_REACH_NLRI
NEXT_HOP: 3.3.3.3
1:1 20.0.0.0/8
R1
1.1.1.1/32
R2
R3
3.3.3.3/32
VPN
  IPv4: 20.0.0.0/8
  RD 1:1
  RT 10:10
BGP-4
MP-BGP

## Slide 17: Comparison Between BGP-4 and MP-BGP Update Messages
MP-BGP defines new fields to carry route prefix and next hop information.
The Update message structures of MP-BGP address families, such as IPv6, VPNv6, and EVPN, are the same.
BGP-4 Update message
Path attributes
NEXT_HOP: 1.1.1.1
NLRI (IPv4)
10.0.0.0/8
MP-BGP Update message
Path attributes
Extended Community
10:10
MP_REACH_NLRI
NEXT_HOP: 3.3.3.3
1:1 20.0.0.0/8
R1
1.1.1.1/32
R2
R3
3.3.3.3/32
10.0.0.0/8
VPN:
  IPv4: 20.0.0.0/8
  RD 1:1
  RT 10:10
BGP-4
MP-BGP

## Slide 18
WAN VPN Overview
MP-BGP Overview
WAN VPN Architecture Fundamentals and Technology Evolution
  MPLS VPN Fundamentals
  WAN VPN Technology Evolution

## Slide 19: Common MPLS VPN Networking
This section uses BGP/MPLS IP VPN as an example to describe MPLS VPN fundamentals.
This example involves four CE sites, with two sites belonging to user X and two sites belonging to user Y. It is required that the sites of one user can communicate with each other but not with those of the other user.
Communication between site A and site B of user X involves two phases: route exchange and data forwarding.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
CE3
CE4

## Slide 20: MPLS VPN Route Advertisement
VPN route advertisement involves the following three phases:
  From the local CE to the ingress PE
  From the ingress PE to the egress PE
  From the egress PE to the remote CE
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
Site A
Site C
Site B
Site D
From the local CE to the ingress PE
From the ingress PE to the egress PE
From the egress PE to the remote CE
CE3
CE4
Route Advertisement
Data Forwarding

## Slide 21: Route Exchange Between CEs and PEs
The CEs and PEs can use static routing, OSPF, IS-IS, or BGP to exchange routes. No matter which routing protocol is used, CEs and PEs exchange standard IPv4 routes.
The local CEs exchange routes with the ingress PE in the same way as the egress PE exchanges routes with the remote CEs.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
BGP, IGP, or static routing
BGP, IGP, or static routing
CE3
CE4
Route Advertisement
Data Forwarding

## Slide 22: Route Transmission from the Ingress PE to the Egress PE — VPN Local Isolation
After receiving routes from CEs, PEs need to independently store routes of different VPNs and solve the problem caused by different customers using overlapping IP address spaces.
The virtual routing and forwarding table (VRF), also called the VPN instance, is used to implement logical isolation between local VPNs.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
Route transmission
192.168.1.0/24
Route transmission
192.168.1.0/24
CE3
CE4
Public network routing table
VPNX routing table
VPNY routing table
Prefix/Mask Outbound Interface
192.168.1.0/24 GE0/0
Prefix/Mask Outbound Interface
192.168.1.0/24 GE0/1
GE0/0
GE0/1
Route Advertisement
Data Forwarding

## Slide 23: RD: Distinguishing Routes During Route Distribution
A VPN instance is only of local significance. It is used to isolate and distinguish routes on the local PE. When a local PE transmits route information to a remote PE, how can the PE distinguish routes with the same prefix? To solve this problem, route distinguishers (RDs) are introduced to distinguish routes with the same prefix and mask but different destinations.
After receiving IPv4 routes from a CE, a PE adds RDs to these routes to convert them into globally unique VPN-IPv4 (VPNv4) routes.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
100:1:192.168.1.0/24
200:1:192.168.1.0/24
RD
IPv4 prefix
CE3
CE4
Route transmission
Converted VPNv4 routes
Route Advertisement
Data Forwarding
Notes: RD, 8 bytes long.
The common RD formats are as follows:
  16-bit AS number:32-bit user-defined number (for example, 100:1)
  32-bit IPv4 address:16-bit user-defined number (for example, 172.1.1.1:1)

## Slide 24: VPNv4 Route Distribution Through MP-BGP
Traditional BGP-4 cannot process VPNv4 routes.
PEs need to establish MP-BGP peer relationships with each other and use MP-BGP to exchange VPNv4 routes.
In this case, PE2 receives VPNv4 routes.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
MP-BGP
VPNv4 Route Distribution Through MP-BGP
CE3
CE4
100:1:192.168.1.0/24
200:1:192.168.1.0/24
Route Advertisement
Data Forwarding

## Slide 25: RT: Controlling Route Import and Export
In this case, PE2 receives two VPNv4 routes and has two VPN instances corresponding to sites B and D respectively. How does PE2 determine the import and export of VPN routes?
The length of an RT is 32 bits. A VPNv4 route can carry one or more RTs. There are two types of RTs: import RT (IRT) and export RT (ERT). When creating a VRF on a PE, you need to specify the IRT and ERT. If an ERT carried in a VPNv4 route received by a PE is the same as an IRT of a local VRF on the PE, the PE imports the route into the VRF.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
MP-BGP
CE3
CE4
100:1:192.168.1.0/24
200:1:192.168.1.0/24
ERT=100:1
ERT=200:1
Routes carrying RTs
VPNX routing table
IRT=100:1
Route Advertisement
Data Forwarding

## Slide 26: Route Transmission from the Egress PE to the Remote CE
PE2 removes the RD from VPNv4 routes and advertises them to the corresponding CEs.
Similarly, other sites also advertise routes to each other. In this way, different sites of the same user are routable to each other.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
MP-BGP
192.168.1.0/24
192.168.1.0/24
Note that route reachability does not mean data reachability.
CE3
CE4
Route Advertisement
Data Forwarding

## Slide 27: Problems Encountered During Data Forwarding
MPLS VPN backbone network
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
IP header
Destination: 192.168.1.1
Data
P
PE2
PE1
IP headers do not carry VPN information, and therefore PEs cannot distinguish the VPNs to which the data belongs.
CE3
CE4
The P does not have any VPN route and therefore cannot forward packets based on IP addresses.
Data forwarding
Route Advertisement
Data Forwarding

## Slide 28: Problem Solving with Two Layers of Labels
MPLS VPN backbone network
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
P
PE2
PE1
IP header
Destination: 192.168.1.1
Data
Inner label: 8888
Outer label: 6662
The inner label (VPN label) is distributed by MP-BGP of each PE to a VPN route. Each PE determines the VPN to which the data belongs according to the inner label.
IP header
Destination: 192.168.1.1
Data
Inner label: 8888
Outer label: 6661
IP header
Destination: 192.168.1.1
Data
The outer label (public network label) is distributed by LDP to the next hop (usually an interface address of a PE) of the VPN route. The P forwards data to a PE according to the outer label.
Public network tunnel
VPN traffic
CE3
CE4
Route Advertisement
Data Forwarding

## Slide 29: Two-layer label distribution and tunnel recursion
Outer label: LDP runs between the PEs and P to allocate labels for the establishment of LSPs between the PEs.
Inner label: PEs establish an MP-BGP peer relationship with each other and allocate inner labels to differentiate data of different VPNs.
Route recursion to tunnels: After receiving VPNv4 routes, the egress PE performs VPN route leaking and recurses these routes to tunnels.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
100:1:192.168.1.0/24
RT=100:1
NextHop=1.1.1.1
Label=8888
RT=100:1
Loopback 0:
1.1.1.1/32
LDP
-------------------------------
LDP LSP
-------------------------------
FEC Out Label
1.1.1.1/32 6662
Note: Only key information is displayed here.
CE3
CE4
Route Advertisement
Data Forwarding
Notes: PEs can allocate VPN labels in either of the following ways:
  Route-based MPLS label allocation: Each route in the VPN instance is assigned a label (one label per route). The disadvantage of this method is that when there are a large number of routes, more entries need to be maintained in the Incoming Label Map (ILM) table of the device, which increases the requirement on device capacity.
  VPN instance-based MPLS label allocation: A label is allocated to the entire VPN instance. All routes in the VPN instance share the same label. The advantage of using this allocation method is that label resources are conserved.
VPN route leaking: VPNv4 routes are matched against the VPN targets of the local VPN instance. After receiving a VPNv4 route, the PE directly imports the route to the local VPN instance without preferentially selecting the route or checking whether the tunnel to which the route recurses exists.
Recursion to tunnels: To transmit VPN traffic to the other end through the public network, a public network tunnel is required to carry the VPN traffic. Therefore, after VPN routes are leaked, routes need to recurse to tunnels based on the destination IPv4 prefix. That is, the next hop of the IPv4 route has a corresponding LSP. The route is added to the routing table of the corresponding VPN instance only if the route can successfully recurse to a tunnel.

## Slide 30: Data Forwarding Process
The following uses packet forwarding from CE3 to CE1 as an example.
MPLS VPN backbone network
P
PE2
PE1
CE1
CE2
192.168.1.0/24
Site A of user X
Site C of user Y
Site B of user X
Site D of user Y
CE3
CE4
1. CE3 sends a common IP packet.
IP packet
IP packet
8888
6662
IP packet
8888
3
IP packet
2. PE2 queries the VPN forwarding table and adds inner label 8888 to the packet. Then, PE2 recurses the corresponding route to a tunnel and adds outer MPLS label 6662 to the packet before forwarding the packet.
3. The P swaps the outer label and forwards the packet to PE1.
4. PE1 removes the labels and forwards the packet to CE1.
Route Advertisement
Data Forwarding

## Slide 31: MPLS VPN Summary
As one of the most typical WAN VPNs, the MPLS VPN with an architecture of separated forwarding and control planes is widely used in the industry.
The control plane uses MP-BGP to transmit VPNv4 routes and inner labels.
The data plane uses LDP to generate MPLS forwarding tunnels. During data forwarding, outer labels are generated upon tunnel recursion.
Despite the development of WAN VPN technologies, the idea of separating the forwarding plane from the control plane is still used.

## Slide 32
WAN VPN Overview
MP-BGP Overview
WAN VPN Architecture Fundamentals and Technology Evolution
  MPLS VPN Fundamentals
  WAN VPN Technology Evolution

## Slide 33: BGP/MPLS IP VPN Technology Architecture
BGP/MPLS IP VPN is not a single VPN technology. Rather, it is a comprehensive solution that combines multiple technologies, including:
  MP-BGP: transmits site route information between PEs.
  LDP: establishes tunnels between PEs.
  VRF: manages VPN users on PEs.
  Static routing, IGP, or BGP: exchanges route information between PEs and CEs.
MPLS VPN backbone network
P
P
CE
site A
MP-BGP exchanges routing information.
site A
Routing table
VRF manages VPN users.
LDP establishes tunnels between PEs.
CE
Static routing/IGP/BGP
PE
PE

## Slide 34: Abstracted WAN VPN Technology Architecture
The WAN VPN technology architecture, which abstracts key BGP/MPLS IP VPN technologies, consists of four functional modules:
  Service access
  VPN service isolation
  MP-BGP-based route transmission
  Tunnel establishment between PEs
WAN
P
P
PE
PE
CE
site A
3. MP-BGP-based route transmission
site A
Information table
2. VPN service isolation
4. Tunnel establishment between PEs
CE
1. Service access

## Slide 35: WAN Data Plane Development - SR
In the WAN VPN, the data plane is presented as data forwarding tunnels.
Common MPLS and SR forwarding tunnels include MPLS (LDP), MPLS TE, SR-MPLS, and SRv6 tunnels.
Multiple tunneling technologies can be deployed on a WAN, and tunnel policies can be used to determine tunnels for route recursion.
WAN
P
P
PE
PE
MPLS LDP
MPLS TE
SR-MPLS
SRv6
CE
CE
User VPN
Tunnel policy

## Slide 36: WAN Control Plane Development - EVPN
In the WAN VPN, the control plane uses MP-BGP.
The MP-BGP address families gradually evolve from VPNv4, L2VPN, and other address families to the EVPN address family, with EVPN unifying the entire control plane.
The control plane supports route exchange among multiple address families, but only the optimal routes are added to the VPN routing table.
WAN
P
P
PE
PE
CE
CE
EVPN
L2VPN
L3VPNv6
L3VPNv4
User VPN routing table
BGP route selection rules

## Slide 37: Technology Evolution of IP Bearer WANs
MPLS
SR-MPLS
SRv6
Forwarding plane
Control plane
Control plane:
removes LDP/RSVP-TE and uses IGP/BGP to distribute labels.
Removes MPLS labels and forwards the packets through IPv6.
SR-MPLS core values:
Simplifies the control plane.
Introduces the source routing mechanism.
Works with the SDN controller.
Device-centric network model:
Each NE calculates the topology independently.
NEs negotiate to establish LDP/TE LSPs.
With a global perspective, NEs can compute only locally optimal paths.
SRv6 core values:
Provides ubiquitous connectivity.
Unifies network programming models.
Deeply integrates with applications.
IGP + SR Extension
IGP + SR Extension
BGP for Service
BGP for Service
Direct evolution
Payload
IPv6 Header + SRH
BGP_LU (Inter-AS)
Payload
VXLAN/GRE/L2TP,etc
MPLS Labels
Payload
VXLAN/GRE/L2TP,etc
MPLS Labels
Continues to simplify the control plane.
LDP
RSVP-TE
IGP
BGP (L3 Service)
T-LDP (L2 Service)
BGP-LU (Inter-AS)
Notes: Target LDP (T-LDP) is used for L2VPN services and distributes VC labels to L2VPN PWs.
BGP Labeled Unicast (BGP-LU) (RFC 3017) is a routing protocol used in both inter-AS and intra-AS scenarios. It advertises MPLS paths between IGP areas or ASs. These routes may span one or more router hops.

## Slide 38: Best Practices of IP Bearer WANs
Huawei iMaster NCE manages WAN forwarders in a unified manner to enable the SRv6+EVPN-capable intent-driven IP WAN bearer network.
IPv6 service
IPv6 service
IPv4/IPv6 dual-stack access
V6
V6
IPv4/IPv6 dual-stack access
V4
IPv4 service
V4
IPv4 service
SRv6 tunnel
IPV6 VPN
IPV4 VPN
IPV6 VPN
IPV4 VPN
P
PE
PE
EVPN
IPv6 backbone network

## Slide 39
(Short-answer question) What is the relationship between EVPN and L2VPN?( )
(Single-answer question) In a BGP/MPLS IP VPN scenario, which of the following protocols is used to allocate outer labels?( )
  OSPF
  MP-BGP
  MPLS LDP
  RSVP-TE
Notes: L2VPN (VPLS as an example) has many drawbacks, such as complex service deployment, limited network scale, and lack of dual-homing support. The IETF proposes EVPN (RFC 7432) to overcome these drawbacks. EVPN is originally designed as an L2VPN technology based on BGP extensions. However, EVPN also supports L3VPN with protocol extensions.
C

## Slide 40
Depending on IP bearer technologies, WAN VPNs are classified into MPLS VPNs and SRv6 VPNs. With the evolution of IPv6 networks, SRv6 and IPv6 naturally merge with each other. Therefore, SRv6 VPN is an inevitable trend.
The WAN VPN control plane is converging. EVPN, which integrates L2VPN and L3VPN capabilities, is a best practice of WAN VPNs.
The advantages of SR need to be demonstrated through the centralized path computation, global optimization, and other capabilities of the controller. For more information, refer to 05 Segment Routing.