## Slide 1
Datacom
V1.0
Lin Feng /wx993403
2021-05-24
Zhu Shigeng/00261992
New

## Slide 2: MPLS TE Fundamentals and Configurations

## Slide 3
Traffic engineering (TE) allows network nodes to establish data forwarding paths based on available resources on a network and reserve network bandwidth for critical traffic. By dynamically monitoring network traffic and device load and adjusting traffic management, routing, resource constraint, and other parameters in real time, traffic engineering optimizes network resource utilization and prevents traffic congestion arising from load imbalance.
Short for MPLS traffic engineering, MPLS TE establishes constraint-based routed label switched paths (CR-LSPs) and diverts traffic to the CR-LSPs, allowing network traffic to be sent over specified paths.
This course describes the fundamentals and features of MPLS TE.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the functions and implementation of MPLS TE.
  Explain how MPLS TE works and its data forwarding modes.
  Illustrate data protection and recovery of MPLS TE.
  Explain advanced MPLS TE features.

## Slide 5
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 6: Concepts of TE
Network engineering is a process of meeting traffic requirements through network design. In essence, it is a process of planning, designing, and deploying networks based on traffic requirements.
TE allows network nodes to establish data forwarding paths based on available resources on a network and reserve network bandwidth for critical traffic. By dynamically monitoring network traffic and device loads and adjusting traffic management, routing, resource constraint, and other parameters in real time, TE optimizes network resource utilization and prevents traffic congestion arising from load imbalance.
If network engineering is compared to road construction, reconstruction, and expansion, TE plays the roles of relieving traffic congestion and ensuring smooth traffic.
Network engineering
TE
Device arrival
Global network construction using new devices
Traffic and path optimization
Service A
Service B
Notes: The essence of network engineering is to understand network traffic requirements through surveys, and then design and deploy networks according to the actual requirements, which is a process of building new networks.
TE is implemented on existing networks. It optimizes resource configuration and improves network performance through proper traffic planning.

## Slide 7: Why Is Traffic Engineering Used?
Conventional IP network
On a conventional IP network, nodes select the shortest path as the optimal route regardless of factors such as bandwidth. This easily causes the shortest path to be congested with traffic, whereas other available paths are idle.
Post-TE network
By establishing CR-LSPs, TE allows specific traffic to be transmitted along specified paths based on traffic characteristics when traffic arrives at the ingress of CR-LSPs.
TE allows network administrators to deploy different forwarding paths to properly allocate network resources and prevent network congestion.
Path 1
Path 2
Service A
Service B
Service A
Service B

## Slide 8: Major Functions of TE
Path planning
Traffic optimization
Fault protection
Different forwarding paths are planned for different service traffic.
When traffic imbalance occurs due to major events or news, TE diverts some traffic to idle links so that network-wide traffic is properly distributed.
TE supports fast protection switching in the case of a device or link fault.
Service B
Service A
1. Link congestion occurs.
2. Traffic is forwarded over idle links.
1. A link or node fails.
2. Fast traffic switching is performed.

## Slide 9: Overview of MPLS TE
RFC 2702 (Requirements for Traffic Engineering Over MPLS), published in September 1999, elaborates on the necessary conditions for implementing MPLS TE, laying a solid foundation for the development and application of MPLS TE.
MPLS TE can effectively schedule, allocate, and utilize existing network resources and provide bandwidth and QoS guarantee for network traffic without needing to upgrade hardware, thereby minimizing costs. Because MPLS TE is implemented based on MPLS, it is therefore easy to deploy and maintain MPLS TE on existing networks.
MPLS TE is a perfect combination of MPLS and TE and provides E2E service guarantee for core and backbone networks of large network service providers.

## Slide 10: MPLS TE Tunnels
MPLS TE often associates multiple LSPs with a virtual tunnel interface, and such a group of LSPs is called an MPLS TE tunnel.
LSPs in an MPLS TE tunnel are called constraint-based routed LSPs (CR-LSPs).
Constraints include bandwidth constraints and path constraints. A CR-LSP can be successfully established only when the links over which a tunnel traverses satisfies the constraints. Constraints allow services to be better planned based on the existing network conditions.
R1
R2
R3
R4
50 M
50 M
100 M
100 M
On the ingress (R1), create an MPLS TE tunnel that passes through R3, with the destination address being R4's address and bandwidth being 100 Mbit/s.
CR-LSP
Bandwidth constraint
Path constraint

## Slide 11: MPLS TE Implementation
Currently, mainstream MPLS TE implementation modes are as follows:
  Resource Reservation Protocol-Traffic Engineering (RSVP-TE)
    RSVP-TE is an extension of RSVP — Resource Reservation Protocol — designed to support TE.
    RSVP-TE technology is mature and has been applied on a large scale. However, the technology is complex with poor extensibility.
  Constraint-based Routing Label Distribution Protocol (CR-LDP)
    CR-LDP is an extension of LDP.
    CR-LDP technology is not mature and is seldom used. However, it is simple with good extensibility.
  Currently, RSVP-TE is widely used in the industry.
Notes: For details about RSVP-TE, see the section "MPLS TE Fundamentals".

## Slide 12: Major MPLS TE Functions (1)
MPLS TE tunnels support explicit paths, which can include or exclude specific nodes as required.
Explicit paths include strict and loose explicit paths.
Loose explicit path
Strict explicit path
Excluded node
Included node
Shortest path
In loose mode, no specific path is specified, and only the nodes to be included or excluded are specified on the tunnel path.
Tunnel path
Traffic can be transmitted along the yellow path only.
Shortest path
Tunnel path
In strict mode, tunnel paths are fixed.
Notes: When a CR-LSP is set up, you can manually specify the nodes that the CR-LSP must traverse or bypass. The path is called an explicit path in MPLS TE.
For details about explicit paths, see the following sections.
If no explicit path is configured as shown in the preceding two figures, traffic is forwarded along the shortest path. If an explicit path is configured, traffic is forwarded along the configured path.

## Slide 13: Major MPLS TE Functions (2)
MPLS TE supports resource reservation on LSPs to ensure E2E bandwidth.
MPLS TE supports path re-optimization for LSPs upon network resource changes.
MPLS TE supports automatic bandwidth adjustment for LSPs upon bandwidth changes.
100 Mbit/s bandwidth is required.
100 Mbit/s bandwidth is reserved.
100 Mbit/s bandwidth is reserved.
150 M
150 M
300 M
200 Mbit/s bandwidth is required.
150 M
150 M
300 M
200 Mbit/s bandwidth is reserved.
200 Mbit/s bandwidth is reserved.
200 Mbit/s bandwidth is reserved.
The link bandwidth is insufficient.
Notes: As shown in the figure, a tunnel with 100 Mbit/s bandwidth is established. If the bandwidth of the tunnel needs to be increased as services grow but the bandwidth of the links over which the tunnel traverses is insufficient, links are re-selected to establish a tunnel.

## Slide 14: Major MPLS TE Functions (3)
MPLS TE supports the configuration of tunnel priorities. In the scenario where a low-priority tunnel has been established over a path and a higher-priority tunnel is to be established over the same path, if the bandwidth resources of the path are insufficient, the higher-priority tunnel can preempt resources of the low-priority tunnel.
Bandwidth is reserved on the path to set up a tunnel for low-priority services.
Rerouting of low-priority services
Resource preemption by high-priority services
Notes: As shown in the preceding figure, when a tunnel needs to be set up for high-priority services but link resources are insufficient, high-priority services will preempt tunnel resources of lower-priority services. In this case, lower-priority services search for other links and re-establish a tunnel.

## Slide 15: Major MPLS TE Functions (4)
MPLS TE supports setup of E2E CR-LSPs.
MPLS TE supports setup of a backup path in advance. The ingress and egress of the backup path are the same as those of the primary path. When the primary path fails, traffic can be switched to the backup path for forwarding, implementing E2E protection for the primary path.
MPLS TE supports local protection. If a link or node on the primary path fails, fast local traffic switching can be triggered. Traffic is switched to the backup path after the tunnel ingress detects the failure.
Tunnel1
Tunnel2
Tunnel3
Protected node
Notes: Tunnel2 is the backup path of Tunnel1. When Tunnel1 fails, traffic is quickly switched to Tunnel2, implementing E2E protection.
If a link or node fails, the tunnel ingress cannot immediately detect the failure. To ensure normal service transmission, fast reroute (FRR) can be used to rapidly switch traffic to Tunnel3. This allows traffic to be immediately switched away from the local failure point, ensuring traffic forwarding.
Tunnel3 provides local protection for nodes. When an intermediate link or node fails, the ingress cannot immediately detect the failure. In this case, local protection can be used to ensure service continuity. After the ingress detects the failure, traffic is switched to Tunnel2 to implement E2E protection.

## Slide 16: Four Major MPLS TE Components
MPLS TE consists of the following four components:
  Information advertisement component
  Path calculation component
  Signaling component (or path establishment component)
  Packet forwarding component
MPLS TE also supports the following advanced features to enrich the basic functions:
  Fast reroute (FRR)
  Tunnel backup
  Auto bandwidth adjustment
  Path re-optimization
Notes: For details about the four components, see the following sections.

## Slide 17: MPLS TE Implementation Procedure
1
2
3
Constraint information
Constraint information
Constraint information
Constraint information
TEDB
R1
R2
R3
R4
TEDB
R1
R2
R3
R4
1
2
4
IS-IS TE
Path computation
R1
R2
R3
R4
LSP
MPLS domain
4
IP domain
IP domain
Diversion of traffic to a CR-LSP
RSVP-TE
RSVP-TE
RSVP-TE
Path establishment
Resource check
Resource check
Resource reservation
Resource reservation
MPLS TE information advertisement
MPLS TE path computation
MPLS TE path establishment
MPLS TE traffic forwarding
Notes: Information advertisement component: advertises information such as constraints, bandwidth, and colors through OSPF-TE/IS-IS-TE, and generates a traffic engineering database (TEDB) on the ingress.
Path computation component: The ingress uses CSPF to compute an optimal path based on the TEDB.
Path establishment component: establishes CR-LSPs through RSVP-TE based on CSPF path computation results, and checks and reserves resources.
Packet forwarding component: diverts traffic to an MPLS TE tunnel so that the tunnel forwards incoming traffic based on labels.

## Slide 18
Overview of MPLS TE
MPLS TE Fundamentals
  MPLS TE Information Advertisement
  MPLS TE Path Computation
  MPLS TE Path Establishment
  MPLS TE Traffic Forwarding
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 19: MPLS TE Information Advertisement
MPLS TE allows routers to establish paths based on link information, instead of simply forwarding traffic through the shortest IP path.
To enable network devices to compute paths more intelligently, each node on a network needs to know resource distribution on the network. Therefore, the following information needs to be advertised:
  link-state information
  TE metric
  Bandwidth information
  Administrative group
  Shared risk link group (SRLG): A group of links that share a common physical resource (for example, a fiber). Links in an SRLG have the same level of risks. Specifically, if one of the links fails, other links in the SRLG also fail. Specifically, if one of the links fails, other links in the SRLG also fail. It is mainly used to enhance the reliability of TE tunnels.
Notes: SRLG is mainly used in the networking where path protection and local protection are enabled. For details, see the section "MPLS TE Reliability."

## Slide 20: Link-State Information
MPLS TE information advertisement is based on the extension of existing IGPs. As such, information (link-state information) collected by IGPs, such as interface IP addresses, link types, and link costs, is still advertised.
R2
R4
R1
R3
LSA/LSP
LSA/LSP
LSA/LSP
LSA/LSP
OSPF/IS-IS
Link-State Information
TE Metric
Bandwidth Information
Administrative Group
Notes: LSAs/LSPs are link-state information advertised by OSPF/IS-IS, including interface IP addresses, link types, and link costs.

## Slide 21: TE Metric
To enhance the controllability of path computation for TE tunnels, MPLS TE provides the TE metric, allowing the computation process to be independent from IGP-based route computation.
Tunnel1 (TE Metric = 3)
R1
R2
R3
R5
R4
Cost = 1
Cost = 3
Cost = 3
Cost = 2
Cost = 2
If the TE metric of the link is used:
Path: R1 -> R2 -> R3 -> R5
Path cost: 4
A TE tunnel is established between R2 and R5 along the path R2 -> R3 -> R5. When R1 accesses R5:
If the IGP metric of the link is used:
Path: R1 -> R2 -> R4 -> R5
Path cost: 5
Link-State Information
TE Metric
Bandwidth Information
Administrative Group
Notes: In this scenario, traffic is forwarded in forwarding adjacency mode. If traffic is forwarded in forwarding shortcut mode, the path remains as R1 -> R2 -> R4 -> R5. For details, see TE traffic forwarding.
By default, the IGP metric is used. Once the TE metric is enabled, the IGP metric becomes invalid.
If the TE metric is configured on the ingress of a tunnel, only path selection policies of the local tunnel is affected.

## Slide 22: Bandwidth Information (1)
MPLS DiffServ-aware Traffic Engineering (DS-TE) combines MPLS TE and MPLS DiffServ to provide effective QoS guarantee.
  MPLS DS-TE divides the LSP bandwidth into eight parts, each part corresponding to a service class. Such a collection of bandwidths of an LSP or a group of LSPs with the same service class are called a class type (CT). DS-TE maps traffic with the same per-hop behavior (PHB) to one CT and allocates resources to each CT. In this way, traffic with the same per-hop behavior (PHB) is mapped to one CT and resources are allocated to each CT.
  DS-TE supports a maximum of eight CTs, which can be marked as CT0 to CT7.
Bandwidth constraints (BCs): can be classified into BC0 to BC7 based on the CT bandwidth.
Maximum reservable bandwidth: maximum bandwidth that a port can reserve for a tunnel.
In a non-MPLS DS-TE scenario, BC0 is used. CT0 reserves bandwidth during tunnel establishment to provide bandwidth protection for services.
Link-State Information
TE Metric
Bandwidth Information
Administrative Group

## Slide 23: Bandwidth Information (2)
[R1-GigabitEthernet1/0/0]mpls te bandwidth max-reservable-bandwidth 100000
[R1-GigabitEthernet1/0/0]mpls te bandwidth bc0 100000
[R1-Tunnel1] mpls te bandwidth ct0 40000
GE1/0/0
GE1/0/0
R1
R2
Tunnel1
Tunnel2
Links that a tunnel passes through
Tunnel1
Tunnel2
CT0
CT1
CT0
CT1
Actual link bandwidth
Maximum reservable link bandwidth
BC1 bandwidth
BC0 bandwidth
Link-State Information
TE Metric
Bandwidth Information
Administrative Group
Notes: The command output shows that CT bandwidth is the reserved bandwidth set for a tunnel, and the maximum reservable bandwidth and BC bandwidth are the maximum link bandwidth that a tunnel can use.

## Slide 24: Administrative Group Attribute
MPLS TE can mark links with different colors so that tunnels can select paths based on link colors.
Administrative group attribute:
  Also called the color attribute of a link, is used to describe link attributes. It consists of 32 bits (each of which can indicate an attribute of a link) and is configured on a physical interface to manage links with user-defined attributes.
  The link administrative group attribute is used together with affinities to control the paths for tunnels.
GE1/0/0
R1
R2
R3
[R2-GigabitEthernet2/0/0]mpls te link administrative group 10101
[R2-GigabitEthernet3/0/0]mpls te link administrative group 10011
GE1/0/0
GE2/0/0
GE3/0/0
Tunnel1
[R1-GigabitEthernet1/0/0]mpls te link administrative group 10001
Link-State Information
TE Metric
Bandwidth Information
Administrative Group
Notes: Administrative group attribute: also called the color attribute of a link, is used to mark links with different colors. During route selection, paths can be selected based on colors. Administrative group information is advertised along with IGP-TE flooding information.
Each bit of an administrative group can be set or not set. Network administrators can associate an administrative group bit with any required meaning, for example:
  Link bandwidth or performance (such as delay).
  Link function or attribute for management purposes. (For example, it can identify that an MPLS TE tunnel passes through a link or multicast services are transmitted over a link.)

## Slide 25: Affinity
An affinity is a 32-bit vector used to describe the links required by a TE tunnel. Similar to the administrative group attribute, an affinity can be considered as a tunnel color and is configured on the ingress of a tunnel. (Tunnel information is not advertised through an IGP).
The 32-bit mask determines which link attributes are to be checked by a device as well as which attributes a link must have for it to be selected for a tunnel. Data can be properly forwarded only when tunnel colors match link colors.
A path can be selected for a tunnel only when the administrative group attribute of a link matches the affinity of the tunnel to be established over the link.
R1
R2
Tunnel1
Tunnel2
[R1-Tunnel1] mpls te affinity property 10101 mask 11011
[R1-Tunnel2] mpls te affinity property 10011 mask 11101
Link-State Information
TE Metric
Bandwidth Information
Administrative Group

## Slide 26: Example for Selecting Paths Based on Tunnel Attributes (1)
Two tunnels to R3 named Tunnel1 and Tunnel2 are established on R1.
It is required that the affinity and mask of a tunnel be used to match against the administrative group attribute of the link over which the tunnel is to be established so that Tunnel1 on R1 uses one physical link between R2 and R3 and Tunnel2 uses another physical link between R2 and R3.
R1
R2
R3
Interface1
0x10001
Interface3
0x10011
Interface2
0x10101
Administrative group/Link color
Tunnel1
Tunnel2
Question: How can we configure affinities for tunnels so that paths can be selected for the tunnels as required?

## Slide 27: Example for Selecting Paths Based on Tunnel Attributes (2)
After a tunnel is assigned an affinity, a device compares the affinity with the administrative group attribute during path computation to determine whether a link with specified attributes is selected or not. Path selection for a tunnel complies with the following two rules:
  The affinity bit whose mask value is 0 is not compared against the corresponding administrative group attribute bit.
  For the affinity bits whose mask value is 1: If the affinity attribute bit value is 0, the administrative group attribute bit value must also be 0. If the affinity attribute bit value is 1, at least one bit of the administrative group attribute must be 1.
R1
R2
R3
Interface 1
0x10001
Interface 3
0x10011
Interface 2
0x10101
[R1-Tunnel1] mpls te affinity property 10101 mask 11011
[R1-Tunnel2] mpls te affinity property 10011 mask 11101
Tunnel1：
R1 (interface1) R2 (interface2) R3
Tunnel2：
R1 (interface1) R2 (interface3)
R3
Question: When a tunnel from R3 to R1 is created, will the link administrative group attribute be reused?
Notes: For Tunnel1, the affinity attribute is 10101 and the mask is 11011. Therefore, the first two bits and last two bits of the affinity attribute are compared with those of the administrative group attribute. Therefore, the second and fourth bits of the administrative group attribute of the link selected by the tunnel must be 0. At least one of the first and fifth bits must be 1.
For Tunnel2, the affinity attribute is 10011 and the mask is 11101. Therefore, the first three bits and last one bit of the affinity attribute are compared with those of the administrative group. The second and third bits of the administrative group attribute of the link selected by the tunnel must be 0. At least one of the first and fifth bits must be 1.
For tunnels established in different directions, the system compares the affinity attribute of the tunnel with the link administrative group attribute configured on the outbound interface of the device along the tunnel path. Therefore, to establish a tunnel from R3 to R1, you need to reconfigure the administrative group attribute on the outbound interfaces of R3 and R2.

## Slide 28: Who Advertises TE Information?
TE information is mainly advertised using extensions of existing link-state routing protocols, including OSPF TE and IS-IS TE. OSPF TE and IS-IS TE automatically collect TE information and flood it to other nodes on the MPLS TE network.
OSPF TE or IS-IS TE is used only in a single area by default.
OSPF TE
ISIS-TE
The Type 10 Opaque LSA is added to collect and advertise TE information, including the maximum link bandwidth, maximum reservable bandwidth, current reserved bandwidth, and link color.
The Extended IS reachability TLV (Type 22 TLV) is added to carry TE information configured on a physical interface.
The Traffic Engineering router ID TLV (Type 134 TLV) is added. It contains a 4-byte router ID, which is currently used as the MPLS LSR ID.
The Extended IP reachability TLV (Type 135 TLV) is added to carry routing information and extend the route metric (wide metric) range.
Notes: IS-IS metrics are classified into the following types:
  Narrow metric: 6 bits. The link metric ranges from 0 to 63.
  Wide metric: extended from 6 bits to 24 bits. The link metric ranges from 0 to 1677214.
The narrow metric supports only 64 vector values, difficult to meet TE requirements on large networks.
To use IS-IS TE, the wide metric must be supported first. The wide metric is not necessarily related to MPLS TE, but it can enhance the scalability of MPLS TE. During the transition from the narrow metric to the wide metric of an IS-IS network, the compatibility between the metrics needs to be considered.
The Type 135 TLV of the wide metric is sometimes called the IP-Extended TLV. You can run the cost-style { wide | compatible | wide-compatible } command to set the metric style. By default, the cost type of IS-IS routes is narrow.

## Slide 29: When to Advertise Information?
The IGP status changes
The link bandwidth changes
1
GE1/0/0
2
3
IGP TE floods state information at intervals, which can be manually configured.
A link is activated or deactivated.
A link attribute (a parameter configured on an interface, such as the cost or administrative group attribute) changes.
200M
.
.
.
Tunnel1
Tunnel2
Tunnel100
When a large number of tunnels that require bandwidth reservation are created on a node, the node frequently updates information in the TEDB and floods it. MPLS TE provides a bandwidth flooding suppression mechanism to reduce the frequency of TEDB updating and flooding.
The ratio of the bandwidth reserved for an MPLS TE tunnel to the available link bandwidth in the TEDB is greater than or equal to the configured threshold.
The ratio of the bandwidth released by an MPLS TE tunnel to the available link bandwidth in the TEDB is greater than or equal to the configured threshold.
Notes: When the link bandwidth changes, bandwidth information flooding is performed as follows:
  If either of the preceding conditions is met, an IGP floods link bandwidth information, and CSPF updates the TEDB.
  For example, the remaining bandwidth of a link is 200 Mbit/s. If 100 TE tunnels with 2 Mbit/s bandwidth are established on the link and the flooding threshold is set to 10%, bandwidth information is not flooded when tunnels 1 to 9 are established. The bandwidth information (20 Mbit/s in total) of tunnels 1 to 10 is flooded only when tunnel 10 is established. The available bandwidth is 180 Mbit/s. According to the configured flooding threshold, the allowed bandwidth is 18 Mbit/s when the second batch of tunnels are established. Therefore, bandwidth information is not flooded when tunnels 11 to 18 are established. The bandwidth information is flooded only when tunnel 19 is established. The process repeats until tunnel 100 is established.

## Slide 30: Flooding Result - Forming the Same TEDB (1)
After an OSPF-TE or IS-IS TE flooding process is complete, all nodes in the local area generate the same TEDB.
The TEDB contains information such as constraints and bandwidth usage of each link. A node calculates the optimal path to another node in the area based on the information in the TEDB. MPLS TE then establishes a CR-LSP over this optimal path.
The TEDB and IGP LSDB are independent of each other.
  Similarities:
    Both the two databases are generated through IGP-based flooding.
  Differences:
    Content: A TEDB contains TE information in addition to all the information in an LSDB.
    Function: An IGP uses information in an LSDB to calculate the shortest path, while MPLS TE uses information in a TEDB to calculate the optimal path for CR-LSPs.

## Slide 31: Flooding Result - Forming the Same TEDB (2)
R1
R2
Router ID: 1.1.1.1
Router ID: 2.2.2.2
192.168.1.2/30
192.168.1.1/30
GE1/0/0
GE1/0/0
[R1] display mpls te cspf tedb node
Router ID: 1.1.1.1
IGP Type: OSPF Process ID: 1 IGP Area: 0
MPLS-TE Link Count: 1
Link[1]:
OSPF Router ID: 192.168.1.1 Opaque LSA ID: 1.0.0.1
Interface IP Address: 192.168.1.1
DR Address: 192.168.1.2
IGP Area: 0
Link Type: Multi-access Link Status: Active
IGP Metric: 1 TE Metric: 1 Color: 0x10001
Bandwidth Allocation Model : -
Maximum Link-Bandwidth: 50000 (kbps)
Maximum Reservable Bandwidth: 50000 (kbps)
Operational Mode of Router: TE
Bandwidth Constraints: Local Overbooking Multiplier:
BC[0]: 50000 (kbps) LOM[0]: 1
BW Unreserved:
Class ID:
[0]: 50000 (kbps), [1]: 50000 (kbps)
[2]: 50000 (kbps), [3]: 50000 (kbps)
[4]: 50000 (kbps), [5]: 50000 (kbps)
[6]: 50000 (kbps), [7]: 50000 (kbps)
Tunnel1
[R1] display mpls te cspf tedb node
Notes: Color indicates the administrative group attribute of a link.

## Slide 32
Overview of MPLS TE
MPLS TE Fundamentals
  MPLS TE Information Advertisement
  MPLS TE Path Computation
  MPLS TE Path Establishment
  MPLS TE Traffic Forwarding
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 33: Overview of the CSPF Algorithm
IS-IS or OSPF uses SPF to compute the shortest path to a node. MPLS TE uses the Constrained Shortest Path First (CSPF) algorithm to compute the optimal path to a node. The CSPF algorithm computes paths based on the following information:
  Cost (provided by the IGP)
  Bandwidth (maximum reservable link bandwidth, BC bandwidth, and CT bandwidth)
  Link attributes (link color and tunnel color)
Information queried during CSPF algorithm-based path computation:
  Attributes of the tunnel to be established, such as affinity and tunnel bandwidth (configured on the ingress of the tunnel)
  TEDB
Load balancing is unavailable for CSFP, which can provide only one path after computation.
Notes: CSPF is an improved shortest path first algorithm that takes certain constraints into consideration when computing the shortest path to a node. Based on the resource availability and whether the selected part violates user policy constraints, CSPF deletes the nodes and links that do not meet the constraints from the current topology, and then uses the SPF algorithm to compute the shortest path that meets the constraints, including a group of LSR addresses.
The next hop calculated by the SPF algorithm of IS-IS or OSPF is the direct next hop. Each router needs to run the SPF algorithm. The result of CSPF computation is a constraint-compliant explicit route. CSPF computation is usually performed only on the ingress of a to-be-established CR-LSP (ingress of a TE tunnel). On the ingress of a TE tunnel, the route calculated by CSPF provides a logical outbound interface to the destination. Traffic enters a CR-LSP through this logical outbound interface, and this CR-LSP is called a TE tunnel.
The MPLS signaling protocol transmits the explicit path calculated by CSPF to downstream nodes in signaling messages. Then, a TE tunnel is set up along the LSRs on the path. After a TE tunnel is successfully set up, the ingress of the TE tunnel adds an MPLS label to each IP packet that needs to enter the TE tunnel. The IP packets are then forwarded along the MPLS TE tunnel until they reach the egress of the TE tunnel.

## Slide 34: How the CSPF Algorithm Works
The links that do not meet tunnel attribute requirements in the TEDB are excluded.
The SPF algorithm calculates the shortest path to a tunnel destination address.
If multiple paths with the same weight still exist, tie-breaking is performed to select the optimal path.
On the ingress R1, create an MPLS TE tunnel with the destination address being R4's address, bandwidth being 100 Mbit/s, and affinity being black.
R1
R2
R3
R4
100 M
100 M
80 M
100 M
100 M
100 M
100 M
R1
R2
R3
R4
100 M
100 M
100 M
100 M
100 M
100 M
R1
R2
R3
R4
100 M
100 M
100 M
100 M
Tie-breaking

## Slide 35: Tie-breaking of the CSPF Algorithm
The CSPF algorithm provides only one path for a destination after computation. When there are multiple paths that meet the basic conditions, tie-breaking of the CSPF algorithm is required:
  Most-fill: selects the link with the highest ratio of used bandwidth to the maximum reservable bandwidth. This policy enables efficient use of link bandwidth resources.
  Least-fill: selects the link with the lowest ratio of used bandwidth to the maximum reservable bandwidth. This policy enables even use of link bandwidth resources.
  Random: selects a link in a way that allows CR-LSPs to be as evenly distributed among links as possible, regardless of the bandwidth.
The most-fill and least-fill modes take effect only when the bandwidth usage difference between two links exceeds 10%. For example, if the bandwidth usage of link A is 50% and the bandwidth usage of link B is 45% (a 5% difference), the most-fill and least-fill modes do not take effect and the random mode is used.
Notes: A link is selected based on a bandwidth ratio using the tie-breaking mechanism. If the ratios are the same (for example, no reservable bandwidth is available or the bandwidth usage is the same), the first discovered link is used regardless of whether least-fill or most-fill is configured.

## Slide 36: Tie-breaking
If the most-fill mode is configured, the paths R1, R4, R5, and R6 are selected.
If the least-fill mode is configured, paths R1, R2, R3, and R6 are selected.
If the random mode is used, links are selected in a way that allows CR-LSPs to be as evenly distributed among links as possible, regardless of the bandwidth.
By default, the random mode is used.
R1
R2
R3
R4
R5
R6
{Used bandwidth}
{100 M}
{300 M}
(200 M)
(400 M)
(Maximum reservable bandwidth)
(200 M)
(400 M)
(200 M)
(400 M)
Notes: For paths R1, R4, R5, and R6, the ratio of used bandwidth to the maximum reservable bandwidth is 3:4.
For paths R1, R2, R3, and R6, the ratio of used bandwidth to the maximum reservable bandwidth is 1:2.
Therefore, when the most-fill mode is configured, the paths R1, R4, R5, and R6 are selected. When the least-fill mode is configured, the paths R1, R2, R3, and R6 are selected.

## Slide 37: Path Selection
When a CR-LSP is set up, you can manually specify the nodes that the CR-LSP must traverse or bypass. These nodes constitute an explicit path in MPLS TE. Therefore, the explicit path can also be used to control path selection in addition to the CSPF algorithm.
One of the greatest charm of MPLS TE lies in its support for explicit paths. You can define the path of a CR-LSP according to the actual requirements to improve operability and manageability.
An explicit path consists of a series of nodes. Two adjacent nodes on an explicit path are connected in either of the following modes:
  Strict: The two nodes are directly connected.
  Loose: Other routers can exist between the two nodes.
You can run the include or exclude command to configure a CR-LSP to traverse or bypass a node.

## Slide 38: Path Selection - Strict Explicit Path
A strict explicit path means that a hop is directly connected to its next hop.
A strict explicit path precisely controls the path of a CR-LSP.
R1
R2
R4
R3
R5
Strict
ERO
R2 strict
R3 strict
R5 strict
[R1] explicit-path p1
[R1-explicit-path-p1] next hop 10.0.12.2 include strict
[R1-explicit-path-p1] next hop 10.0.23.2 include strict
[R1-explicit-path-p1] next hop 10.0.35.2 include strict
10.0.12.0/30
.1
.2
10.0.23.0/30
.1
.2
10.0.35.0/30
.1
.2
Ingress
LSR
Egress
LSR
Notes: ERO: indicates the explicit route object. It is mainly used to indicate explicit path information.
In the example, "R2 strict" indicates that the CR-LSP must pass through R2 and the previous hop of R2 is Ingress R1. "R5 strict" indicates that the CR-LSP must pass through R5 and the previous hop of R5 is R3.

## Slide 39: Path Selection - Loose Explicit Path
A loose explicit path specifies the nodes through which a CR-LSP must pass; however, other routers can exist between a specified node and its next hop.
R5
R1
R3
R2
R4
Loose
ERO
R4 loose
[R1] explicit-path p1
[R1-explicit-path-p1] next hop 4.4.4.4 include loose
Ingress
LSR
Egress
LSR
LSR ID:4.4.4.4
Notes: In the example, "R4 loose" indicates that the CR-LSP must pass through R4, but other nodes can exist between R4 and Ingress R1.

## Slide 40: Path Selection - Hybrid Explicit Path
The strict mode and loose mode can be used together.
R1
R2
R4
R3
R5
Strict
ERO
R2 strict
R5 loose
R6 strict
[R1] explicit-path p1
[R1-explicit-path-p1] next hop 10.0.12.2 include strict
[R1-explicit-path-p1] next hop 5.5.5.5 include loose
[R1-explicit-path-p1] next hop 10.0.56.2 include strict
10.0.12.0/30
.1
.2
10.0.23.0/30
.1
.2
10.0.35.0/30
.1
.2
Ingress
LSR
Egress
LSR
10.0.56.0/30
R6
.1
.2
Loose
LSR ID:5.5.5.5
Notes: In the example, "R2 strict" indicates that the CR-LSP must pass through R2 and the previous hop of R2 is Ingress R1. "R6 strict" indicates that the CR-LSP must pass through R6 and the previous hop of R6 is R5.
"R5 loose" indicates that the CR-LSP must pass through R5, but a router can be deployed between R5 and Ingress R1, which do not need to be directly connected.
Therefore, the CR-LSP path can be R1 -> R2 -> R3 -> R5 -> R6. It can also be R1 -> R2 -> R4 -> R5 -> R6.

## Slide 41
Overview of MPLS TE
MPLS TE Fundamentals
  MPLS TE Information Advertisement
  MPLS TE Path Computation
  MPLS TE Path Establishment
  MPLS TE Traffic Forwarding
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 42: TE Signaling Protocols
After path computation is complete, TE needs to reserve resources along the path to establish a CR-LSP.
MPLS TE mainly uses RSVP-TE as the signaling protocol to establish CR-LSPs.
RSVP is designed for the integrated service model in the QoS system. It is used to reserve resources on each node along a path. RSVP works at the transport layer and does not participate in the transmission of application data. It is a control protocol on the Internet and is similar to ICMP.
RSVP-TE is an extension to RSVP and sets up or deletes CR-LSPs by using TE attributes carried in extended objects.
R1
R2
R3
RSVP-TE
RSVP-TE
Label
Label
Tunnel
Notes: Currently, RSVP-TE is mainly used as the signaling protocol for MPLS TE, and CR-LDP is seldom used.
As shown in the preceding figure, R1, R2, and R3 use RSVP-TE as the signaling protocol to distribute labels and set up CR-LSPs.

## Slide 43: RSVP Packet Format and Message Type
RSVP is a soft-state protocol. It needs to periodically and repeatedly advertise reservation information on the network.
An RSVP message consists of a common header followed by one or more objects.
Version | Flags | Message Type | RSVP Checksum
Send TTL |  | Reserved | RSVP Length
Object… |  |  | 
Message Type | Name | Function
1 | Path | Used to request downstream nodes to distribute labels for the path.
2 | Resv | Used to reserve resources on each node.
3 | PathErr | Sent upstream by a node if an error occurs during the processing of a Path message.
4 | ResvErr | Sent downstream by a node if an error occurs during the processing of an Resv message.
5 | PathTear | Sent downstream by the ingress to delete information about the local state created on each node of the path.
6 | ResvTear | Sent upstream by the egress to delete the reserved local resources assigned to a path.
Notes: A soft state is a resource reservation state that a node maintains by periodically updating RSVP messages.
Main RSVP-TE messages are described as follows:
  Path message: used to request downstream nodes to distribute labels for a path. A Path message records the path information at each hop of a path and is used to establish a path state block (PSB) at a hop.
  A Resv message carries the resource reservation information required by a sender and is sent in the reverse direction of data flows. The Resv message is used by each node on a path to establish a reservation state block (RSB) and record information about distributed labels.
  PathErr message: sent upstream by an RSVP node if an error occurs during the processing of a Path message. A PathErr message is forwarded upstream by each transit node until it arrives at the ingress.
  ResvErr message: sent downstream by an RSVP node if an error occurs during the processing of a Path message. A ResvErr message is forwarded downstream by each transit node until it arrives at the egress.
  ResvTear message: sent upstream by the egress to delete the reserved local resources assigned to a path.
  ResvTear message: sent upstream by the egress to delete the local reserved resources assigned to a path. After receiving the ResvTear message, the ingress sends a PathTear message to the egress.

## Slide 44: How RSVP Works
RSVP has three basic functions:
  Path establishment and maintenance
  Path teardown
  Error advertisement
The signaling process of RSVP is as follows:
  The start point sends a Path message to the end point to apply for resource reservation, and the end point sends an Resv message to complete resource reservation.
R1
R2
R3
Path
Resv
Path
Resv
Notes: RSVP is a soft-state signaling protocol used to reserve network resources periodically.
As shown in the preceding figure, R1 sends a Path message downstream to apply for resource reservation. After receiving the message, R2 forwards the Path message downstream until the tunnel egress (R3) receives the message. R3 then generates an Resv message based on the Path message and sends the Resv message upstream until the ingress receives the Resv message while completing resource reservation on the link.

## Slide 45: New Objects Extended by RSVP-TE (1)
RSVP-TE extends TE CR-LSPs through extended objects:
  Supports label distribution in downstream on demand (DoD) mode.
  Allocates network resources to explicit CR-LSPs.
  Supports teardown of a CR-LSP in make-before-break (MBB) mode when the established CR-LSP is preempted.
  Records each node that a CR-LSP passes through to prevent loops.
  Supports diagnosis of CR-LSPs.
Notes: Detailed extended functions will be described in subsequent courses.
The basic principle of MBB is as follows: A new CR-LSP is established first. After all traffic is switched to this CR-LSP, the original CR-LSP is torn down to ensure the forwarding of service traffic.

## Slide 46: New Objects Extended by RSVP-TE (2)
Label_Request
Label
Explicit_Route
Record_Route
Session_Attribute
Sender_Template
Filter_Spec
Session
Flowspec
Sender_Tspec
Version | Flags | Message Type | RSVP Checksum
Send TTL |  | Reserved | RSVP Length
Object… |  |  | 
Length | Class Num | C-Type
Object Content |  | 

## Slide 47: New Objects Extended by RSVP-TE (3)
Object Type | RSVP Information | Description
Label_Request | Path | Identifies the LABEL_REQUEST object.
Label | Resv | Carries an assigned label.
Explicit_Route | Path | Explicit Route Object (ERO) describes information about the path through which a CR-LSP passes. The path can be a strict or loose one.
Record_Route | Path, Resv | Record Route Object (RRO) is a list of CR-LSRs through which a Path message passes.
Session_Attribute | Path | Specifies attributes, such as the setup priority, hold priority, reservation style, and affinity.
Sender_Template | Path | Carries the IP address and LSP ID of the node that sends the message.
Filter_Spec | Resv | Carries the IP address and LSP ID of the node that sends the message.
Session | Path, Resv | Carries RSVP session information, such as the destination address, tunnel ID, and extended tunnel ID.
Flowspec | Resv | Specifies QoS parameters for a data flow.
Sender_Tspec | Path | Specifies traffic characteristics of a data flow.

## Slide 48: MPLS TE Tunnel
An MPLS TE tunnel is a head-end CR-LSP initiated by the ingress of a tunnel.
RSVP-TE uses CSPF to compute a path, and the receiver initiates a resource reservation request for the path. RSVP-TE uses Path and Resv messages to request CR-LSP establishment and maintain resource reservation information.
An MPLS TE tunnel is unidirectional.
R1
R2
R3
R5
R6
R4
1
2
POP
100
101
102
Path message: requests the egress to initiate resource reservation and set ERO.
Resv message: reserves bandwidth resources and allocates labels.
Notes: Note that an MPLS TE tunnel is unidirectional. When bidirectional mutual access services exist, two CR-LSPs in opposite directions need to be established to forward traffic.

## Slide 49: Process of Establishing an MPLS TE Tunnel (1)
After RSVP-TE is configured on the ingress, the ingress creates a path state block (PSB) and sends a Path message to downstream nodes.
  The Path message carries the information required for establishing a tunnel, such as the ingress, egress, ERO, and reserved bandwidth of the tunnel.
  The PSB is used to record path information of each node.
After receiving the Path message, the transit node processes and forwards this message, and creates a PSB based on the message.
After receiving the Path message, the egress creates a PSB.
R1
R2
R3
Ingress
Egress
Path
PSB
Path
PSB
PSB
Transit

## Slide 50: Process of Establishing an MPLS TE Tunnel (2)
<R1>display mpls rsvp-te psb-content
-----------------------------------------------------------------------------
The PSB Content
------------------------------------------------------------------------------
Tunnel Addr: 3.3.3.3 Exist time: 19h 29m 46s
Tunnel ExtID: 1.1.1.1 Session ID: 116
Ingress LSR ID: 1.1.1.1 Local LSP ID: 34926
Previous Hop: ---- Next Hop: 10.0.12.2
Incoming / Outgoing Interface: ---- / GigabitEthernet1/0/0
InLabel: NULL OutLabel: 32846
Send Message ID: 0 Recv Message ID: 0
Session Attribute:
SetupPrio: 7 HoldPrio: 7
SessionAttrib: SE Style desired
CSPF Route Flag: False
LSP Type: -
FRR Flag: No protection Local RRO Flag: 0x0
FRR Mode: -
ERO Information:
L-Type ERO-IPAddr ERO-PrefixLen Label
ERHOP_STRICT 10.0.12.2 32
ERHOP_STRICT 10.0.23.1 32
ERHOP_STRICT 10.0.23.2 32
…
CT-BandWidth Information(Bytes/sec):
CT0 Bandwidth: 0 CT1 Bandwidth: 0
CT2 Bandwidth: 0 CT3 Bandwidth: 0
CT4 Bandwidth: 0 CT5 Bandwidth: 0
CT6 Bandwidth: 0 CT7 Bandwidth: 0
Path Message arrive on Unknown(0x0) from PHOP 0.0.0.0
Path Message sent to NHOP 10.0.12.2 on GigabitEthernet1/0/0
Resource Reservation OK
PADS Ability: Enable
Notes: Tunnel Addr: destination address of a tunnel.
Tunnel ExtID: extended ID of a tunnel.
Exist time: length of time since the PSB information was generated.
Ingress LSR ID: ID of the ingress.
Local LSP ID: ID of the local CR-LSP.
Session Attribute: attributes of an RSVP session.
SetupPrio: session setup priority.
HoldPrio: session hold priority.
SessionAttrib: RSVP session attribute.
  SE Style desired: The expected resource reservation style is shared explicit (SE).
  FF Style desired: The expected resource reservation style is fixed filter (FF).
  Label Record: enables the label record function when exchanging Path and Resv messages.
  Local Protection desired: provides CR-LSPs with FRR protection.
  Node Protection desired: provides CR-LSPs with node protection.
  Bandwidth Protection desired: provides LSPs with bandwidth protection.
  Path Re-evaluation desired: Path re-evaluation is required for the CR-LSP.

## Slide 51
Notes: ERO Information: explicit route object (ERO).
  SE Style desired: The expected resource reservation style is SE.
  ERO-IPAddr: explicit route address.
  ERO-PrefixLen: explicit route prefix length.
  Label: ERO-Label.
CT-BandWidth Information: CT and corresponding bandwidth information.
CT0 Bandwidth: CT0 bandwidth.

## Slide 52: Tunnel Resource Reservation Style
A reservation style defines how an RSVP node reserves resources after receiving a request sent by an upstream node. The NE40E supports the following reservation styles:
  Fixed filter (FF): creates an exclusive reservation for each sender, which does not share its resource reservation with other senders and is assigned a unique label.
  Shared explicit (SE): explicitly specifies the senders in a reservation for receivers. These senders share one reservation but send different labels to a receiver.
The SE style allows old and new tunnels of the same session to share bandwidth resources. The old tunnel is torn down only after all traffic of the old tunnel is switched to the new tunnel.
The SE style is an important condition for implementing make-before-break.
Notes: How to determine whether the old and new tunnels belong to the same session
  A unique identifier is obtained based on 5-tuple information {sender address, LSP ID, endpoint address, tunnel ID, and extended tunnel ID}.
  The rules for MPLS TE SE reservation are as follows: If two reservations have the same 5-tuple information except for the LSP ID, the two reservations belong to the same session and can share bandwidth resources.
The 5-tuple elements are contained in the Session and Sender_Template objects.
  Session object
    Endpoint address: RID of the tunnel endpoint
    Tunnel ID: number of the configured TE tunnel
    Extended tunnel ID: The default value is usually 0.
  Sender_Template object
    Sender address: RID of the tunnel ingress
    LSP ID: functions as an instance counter. The LSP ID increases by 1 each time the bandwidth requirement of a tunnel changes or a new path is used.

## Slide 53: Process of Establishing an MPLS TE Tunnel (3)
After receiving a Path message, the egress generates an Resv message based on the Path message, creates a Reserve State Block (RSB), and sends the Resv message upstream.
  The Resv message carries resource reservation information requested by the sender, such as labels and reserved bandwidth.
  The RSB is mainly used to record information about allocated labels.
The transit node processes and forwards the Resv message and creates state blocks such as the RSB.
After receiving the Resv message, the ingress creates an RSB and confirms that the resources are successfully reserved.
The label distribution on the path is complete, and the CR-LSP is set up.
R1
R2
R3
Ingress
Egress
Resv
RSB
RSB
RSB
Resv
Transit
CR-LSP

## Slide 54: Process of Establishing an MPLS TE Tunnel (4)
<R1> display mpls rsvp-te rsb-content
------------------------------------------------------------------------------
The RSB Content
------------------------------------------------------------------------------
Tunnel Addr: 3.3.3.3 Session Tunnel ID: 1
Tunnel ExtID: 1.1.1.1
Next Hop: 10.0.12.2 Reservation Style: SE Style
Reservation Incoming Interface: GigabitEthernet1/0/0
Reservation Interface: GigabitEthernet1/0/0
Message ID: 0
Filter Spec Information-
The filter number: 1
Ingress LSR ID: 1.1.1.1 Local LSP ID: 24 OutLabel: 32846
Resv Message arrive on GigabitEthernet1/0/0 from NHOP 10.0.12.2
<R3> display mpls rsvp-te rsb-content
Tunnel Addr: 3.3.3.3 Session Tunnel ID: 1
Tunnel ExtID: 1.1.1.1
Next Hop: ----- Reservation Style: SE Style
Filter Spec Information-
The filter number: 1
Ingress LSR ID: 1.1.1.1 Local LSP ID: 24 OutLabel: NULL
Resv Message arrive on Unknown from NHOP 0.0.0.0
<R2> display mpls rsvp-te rsb-content
Tunnel Addr: 3.3.3.3 Session Tunnel ID: 1
Tunnel ExtID: 1.1.1.1
Next Hop: 10.0.23.2 Reservation Style: SE Style
Filter Spec Information-
The filter number: 1
Ingress LSR ID: 1.1.1.1 Local LSP ID: 24 OutLabel: 3
Resv Message arrive on GigabitEthernet1/0/0 from NHOP 10.0.23.2
Notes: OutLabel: indicates the outgoing label.

## Slide 55: Bidirectional CR-LSP
When bidirectional services exist, two MPLS TE tunnels can be deployed on two devices that are the source and sink of each other to form a bidirectional CR-LSP to carry bidirectional traffic and ensure bandwidth.
The two tunnels are independent of each other. When traffic switching is performed on one tunnel upon a fault, the other tunnel cannot be notified of the fault in time to also perform traffic switching. As a result, services are interrupted.
CR-LSP
CR-LSP
R1
R2
Notes: If no reverse MPLS TE tunnel is configured, the traffic from R2 to R1 can be forwarded only through routes, and bandwidth protection cannot be provided. As a result, congestion cannot be avoided.

## Slide 56: Bidirectional Associated CR-LSP
If a pair of MPLS TE CR-LSPs in opposite directions is established between two nodes and each CR-LSP is bound to the ingress of its reverse LSP, the two LSPs form a bidirectional associated LSP. The associated bidirectional CR-LSP is configured to prevent traffic congestion. If a fault occurs on one end, the other end is notified of the fault so that both ends trigger traffic switching at the same time to ensure that bidirectional services are not interrupted.
R1
R2
R3
R4
Tunnel1:
Ingress LSR ID = 1.1.1.1
Tunnel ID = 100
My Bidirectional Associated Label Switch Path is:
Tunnel 2 Ingress LSR ID = 4.4.4.4
Tunnel ID = 200
Tunnel2:
Ingress LSR ID = 4.4.4.4
Tunnel ID = 200
My Bidirectional Associated Label Switch Path is:
Tunnel 1 Ingress LSR ID = 1.1.1.1
Tunnel ID = 100
1.1.1.1
4.4.4.4
Notes: Tunnel1 and Tunnel2 must both be MPLS-TE tunnels. They can be either dynamic CR-LSPs established using RSVP-TE or static CR-LSPs manually configured.
The tunnel ID and ingress LSR ID of the reverse CR-LSP are specified on each tunnel interface so that the forward and reverse CR-LSPs are bound to each other. A reverse LSP must be specified for both the ingress and egress of a tunnel. In addition, the binding relationships must match each other. For example, in the preceding figure, set the reverse tunnel ID to 200 and ingress LSR ID to 4.4.4.4 on Tunnel1 so the reverse tunnel is bound to Tunnel1.
R1 and R4 are ingress LSRs or egress LSRs for forward and reverse LSPs.

## Slide 57: Static Bidirectional Co-routed CR-LSP
Forward and reverse service traffic is usually required to be transmitted along the same path on a network where no routing protocol runs. In this context, the static bidirectional co-routed CR-LSP is proposed to ensure that MPLS technology can still be used.
A static bidirectional co-routed LSP is a type of manually configured LSP over which two flows are transmitted in opposite directions by the same nodes over the same links.
Ingress
Transit
Egress
In-label | Null
Out-label | 20
CT0 bandwidth | 10000
In-label | 20
Out-label | 40
CT0 bandwidth | 10000
In-label | 40
Out-label | Null
CT0 bandwidth | Null
Forward LSP
Tunnel1
Network administrator
In-label | 20
Out-label | Null
CT0 bandwidth | Null
In-label | 16
Out-label | 20
CT0 bandwidth | 10000
In-label | Null
Out-label | 16
CT0 bandwidth | 10000
Reverse LSP
Tunnel2
Network administrator
Ingress
Transit
Egress
GE1/0/0
GE1/0/0
GE1/0/0
GE1/0/1
Notes: As shown in the preceding figure, a network administrator manually configures the incoming and outgoing labels of each node on the forward and reverse LSPs and sets the bandwidth (CT0 bandwidth) required by the LSPs. The bandwidth must be less than or equal to the available bandwidth of the outbound interface of each LSP. Therefore, for the forward LSP, the CT0 bandwidth does not need to be configured on the egress. For the reverse LSP, the CT0 bandwidth does not need to be configured on the ingress.
A static bidirectional co-routed CR-LSP is one LSP and corresponds to two forwarding entries. It can go up only when the conditions for forwarding traffic in both directions are met. If the conditions for forwarding traffic in one direction are not met, the LSP is in the Down state. In addition, the forwarding entries in both directions are associated with each other. When IP forwarding capabilities are unavailable, any transit node can send back a response packet along the original path. Compared with two independent LSPs in opposite directions, a static bidirectional co-routed LSP has the same delay and jitter in both directions, which guarantees QoS for bidirectional services.
To establish a static bidirectional co-routed LSP, you need to manually specify labels and forwarding entries mapped to two forwarding equivalence class (FEC) for traffic transmitted in opposite directions.
A static bidirectional co-routed LSP is meaningful only to the local node, and the local node cannot be aware of the entire LSP. You need to select the direction from the ingress to the egress as the forward direction, and the other direction becomes the reverse direction.

## Slide 58
Notes: The process of establishing a static bidirectional co-routed LSP is as follows:
  On the ingress of the static bidirectional co-routed LSP, configure a tunnel interface and enable MPLS TE on the outbound interface. If the outbound interface is up and has available bandwidth greater than or equal to the LSP bandwidth, the static bidirectional co-routed LSP is up after being bound to the tunnel interface, regardless of whether a transit node or the egress exists.
  On each transit node of the static bidirectional co-routed LSP, enable MPLS TE on the outbound interface. If the outbound interface is up and the available bandwidth in both directions is greater than or equal to the LSP bandwidth, the static bidirectional co-routed LSP is up, regardless of whether the ingress, egress or other transit nodes exist.
  On the egress of the static bidirectional co-routed LSP, enable MPLS TE on the inbound interface. If the inbound interface is up and has available bandwidth greater than or equal to the LSP bandwidth, the static bidirectional co-routed LSP is up after being bound to the tunnel interface, regardless of whether the ingress or a transit node exists.

## Slide 59
Overview of MPLS TE
MPLS TE Fundamentals
  MPLS TE Information Advertisement
  MPLS TE Path Computation
  MPLS TE Path Establishment
  MPLS TE Traffic Forwarding
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 60: MPLS TE Traffic Forwarding
An MPLS TE tunnel is established through information advertisement, path selection, and path establishment. Different from LDP, the LSP established by MPLS TE cannot automatically import traffic to the tunnel for forwarding. Traffic needs to be imported to the MPLS TE tunnel using a certain mode, so that the device can forward traffic based on labels.
Traffic can be imported to an MPLS TE tunnel using:
  Static route
  Auto route
  Policy-based routing (PBR)
Notes: Unlike LDP, MPLS TE can forward traffic independently. TE requires manual configuration to forward traffic.

## Slide 61: Forwarding Based on the Static Route (1)
The simplest way to divert traffic to a TE tunnel is to configure a static route. Such a static route works in the same way as common static routes. You only need to configure the TE tunnel interface as the outbound interface of the static route.
TE tunnel forwarding supports recursive static routes.
As shown in the figure, a TE tunnel is established between R1 and R7. Tunnel1 is configured as the tunnel interface on R1. A static route is configured on R1 to divert traffic from R1 to R9 to the tunnel (the cost of each link is 10).
R1
R2
R3
R4
R5
R6
R7
R8
R9
Tunnel1
9.9.9.9
Egress
Ingress
[R1] ip route-static 9.9.9.9 255.255.255.255 Tunnel1
Notes: Recursive static route: The next hop of the destination of the static route is not the TE tunnel interface. The TE tunnel interface is only an intermediate link to the destination. Simply put, route recursion needs to be performed on the TE tunnel to reach the next hop of the destination.

## Slide 62: Forwarding Based on the Static Route (2)
The routing table of R1 shows that the traffic from R1 to R9 is forwarded through the TE tunnel, but the traffic from R1 to R7 is still forwarded through an IGP, even if R7 is the endpoint of the tunnel.
R1
R2
R3
R4
R5
R6
R7
R8
R9
Tunnel1
9.9.9.9
Egress
Ingress
[R1] display ip routing-table
Question: How can all service traffic from R1 to R7 be forwarded through the tunnel without the need to configure too many static routes?
Destination | Nexthop | Cost
R2 | R2 | 10
R3 | R3 | 10
R4 | R3 | 20
R5 | R2 | 20
R6 | R2 | 30
R7 | R2 | 30
R8 | R2 | 40
R9 | Tunnel1 | 40

## Slide 63: Forwarding based on the Auto Route
Auto route: A TE tunnel is considered as a logical link participating in IGP route calculation. In this case, the tunnel interface is used as the outbound interface of a route, eliminating the need for a large number of manual configurations involved in static routes.
A TE tunnel can be used as a P2P link during IGP route calculation. You can configure a TE metric for the TE tunnel, which allows for more controllability during path selection of nodes.
Auto route forwarding modes:
  IGP shortcut
  Forwarding adjacency
Notes: The configuration of static route forwarding is complex, and the workload is heavy. Like a routing protocol, auto route allows traffic to be automatically forwarded in a tunnel.

## Slide 64: IGP Shortcut
In IGP shortcut mode, the TE LSP link is not advertised to neighboring nodes. Therefore, the tunnel can be used only by the ingress of the tunnel, not by other nodes.
R1
R2
R3
R4
R5
R6
R7
R8
R9
Tunnel1
Egress
Ingress
[R1] display ip routing-table
[R3] display ip routing-table
[R3] interface tunnel 1
[R3-Tunnel1] mpls te igp shortcut isis
[R3-Tunnel1] mpls te igp metric absolute 10
[R3-Tunnel1] isis enable
Cost of each interface = 10
Destination | Next hop | Cost
R5 | R2 | 20
R6 | R2 | 30
R7 | R2 | 30
Destination | Next hop | Cost
R5 | Tunnel1 | 20
R6 | Tunnel1 | 30
R7 | Tunnel1 | 30
Notes: IGP shortcut affects only the local routing policy and does not affect the routing of other routers.
The IGP metric of the TE tunnel is configured using the mpls te igp metric { absolute | relative } value command.
  If absolute is configured, the metric of the TE tunnel is the configured value.
  If relative is configured, the metric of the TE tunnel is the sum of the metric of the corresponding IGP path and relative metric.

## Slide 65: Forwarding Adjacency
On a live network, MPLS TE is usually deployed only on a few core nodes. In this case, edge nodes cannot detect the existence of TE tunnels and can only select paths based on the traditional IGP.
In forwarding adjacency mode, the TE LSP is advertised to neighboring nodes. Therefore, all nodes can use this tunnel.
If forwarding adjacency is used, the ingress and egress of a tunnel must be in the same area.
R1
R2
R3
R4
R5
R6
R7
R8
R9
Tunnel1
TE metric = 5
Egress
Ingress
[R1] display ip routing-table
[R3] interface tunnel 1
[R3-tunnel1] mpls te igp advertise
[R3-tunnel1] mpls te igp metric absolute 5
[R3-tunnel1] isis enable
Cost of each device interface = 10
destination | nexthop | cost
R5 | Tunnel1 | 5
R6 | Tunnel1 | 15
R7 | Tunnel1 | 15
destination | nexthop | cost
R5 | R3 | 15
R6 | R3 | 25
R7 | R3 | 25
[R3] display ip routing-table

## Slide 66: Policy-Based Routing (PBR)
TE policy-based routing is simple and does not change the routing table. Traffic is forwarded based on the configured policy. If packets do not match PBR rules, they are forwarded in IP forwarding mode; if they match PBR rules, they are forwarded over specific tunnels.
R1
R2
R3
R4
R5
R6
R7
R8
R9
Tunnel1
Egress
Ingress
[R1] policy-based-route set_tunnel permit node 1 map-instance 1
[R1-policy-based-route-set_tunnel-1] if-match acl 3000
[R1-policy-based-route-set_tunnel-1] apply output-interface Tunnel1
Notes: ACL 3000 is defined according to the actual situation.

## Slide 67: L2/L3VPN over TE
In addition to the preceding MPLS TE traffic forwarding modes, tunnel recursion can be configured to divert service traffic to TE tunnels for forwarding in L2/L3VPN over TE scenarios.
As shown in the figure, CE1 and CE2 belong to the same L3VPN and access the backbone network through PE1 and PE2, respectively. A TE tunnel is set up between PE1 and PE2. It is required that a tunnel policy be configured to divert traffic from CE1 to CE2 to the TE tunnel when the traffic reaches PE1.
PE1
PE2
CE1
CE2
P1
Tunnel1
G1/0/0
[PE1] tunnel-policy policy1
[PE1-tunnel-policy-policy1] tunnel select-seq cr-lsp load-balance-number 1
Configure a tunnel policy named policy1 to select CR-LSPs for traffic forwarding, and set the number of tunnels participating in load balancing to 1:
Configure L3VPN access on PE1 and apply the tunnel policy:
[PE1] ip vpn-instance vpn1
[PE1-vpn-instance-vpn1] ipv4-family
[PE1-vpn-instance-vpn1-af-ipv4] tnl-policy policy1
[PE1] interface gigabitethernet 2/0/0
[PE1-GigabitEthernet2/0/0] ip binding vpn-instance vpn1

## Slide 68
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
  Path Protection
  Local Protection (FRR)
  MPLS TE Tunnel Protection Group
  Fault Detection
Advanced MPLS TE Features

## Slide 69: Path Protection Overview
Path protection is also called E2E protection. A backup CR-LSP is set up to protect traffic on the primary CR-LSP.
Path protection establishes multiple CR-LSPs between the ingress and egress of a tunnel, with each CR-LSP traversing a different path.
If the ingress detects that the primary CR-LSP is unavailable, the ingress switches traffic to a backup CR-LSP. After the primary CR-LSP recovers, traffic is switched back.
CR-LSP backup is performed in either of the following modes:
  Hot standby
  Ordinary backup
Hot standby can be used together with fault detection technology (BFD) to switch traffic to the backup path within 50 ms. In ordinary backup mode, the switchover time depends on the number of affected tunnels when a fault occurs.

## Slide 70: Hot Standby
A backup CR-LSP is set up immediately after the primary CR-LSP is set up. When a message indicating that the primary CR-LSP fails is received by the ingress, traffic is switched to the backup CR-LSP. After the primary LSP recovers, traffic is switched back.
Hot-standby CR-LSPs support best-effort paths. When both the primary and backup CR-LSPs fail, a temporary CR-LSP can be set up, and traffic is switched to the best-effort path.
R1
R2
R3
R4
Primary path
Backup path
Best-effort path
R1
R2
R3
R4
R1
R2
R3
R4
Service traffic
Notes: The primary and backup CR-LSPs can be specified using explicit paths. The best-effort path is automatically calculated by the system based on network faults and varies according to faulty nodes.

## Slide 71: Ordinary Backup
When the ingress receives a message indicating that the primary CR-LSP fails, the ingress initiates the setup of a backup CR-LSP. After the backup CR-LSP is set up, traffic is switched to the backup CR-LSP. After the primary CR-LSP recovers, traffic is switched back.
Common backup CR-LSPs do not support best-effort paths.
R1
R2
R3
R4
R1
R2
R3
R4
Primary path
Backup path
Service traffic

## Slide 72
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
  Path Protection
  Local Protection (FRR)
  MPLS TE Tunnel Protection Group
  Fault Detection
Advanced MPLS TE Features

## Slide 73: Limitations of Path Protection
Path protection provides E2E protection for TE tunnels. If a node or link on a tunnel fails, traffic is switched to a backup path. This process involves IGP route re-convergence on the backup path, CSPF path recalculation, and CR-LSP re-establishment. The slow process may cause packet loss.
Fast reroute (FRR), also called local protection, is a temporary protection measure. When a transit node fails, local protection is triggered and a backup CR-LSP is set up locally for traffic switching. At the same time, the ingress of the tunnel is instructed to recalculate paths and switch traffic to the backup path in time.
Primary CR-LSP
Service traffic
Configure FRR
to trigger local protection.
Notes: FRR is a temporary protection measure. Compared with path protection, FRR allows traffic switching to be performed more quickly.

## Slide 74: Related FRR Concepts (1)
FRR can be classified into the following protection modes by tunnel establishment method:
  One-to-one backup
  Facility backup
The roles of devices in FRR can be classified into the following types:
  Point of local repair (PLR): ingress of the backup CR-LSP. The ingress must be on the path of the primary CR-LSP and cannot be the egress of the primary CR-LSP.
  Merge point (MP): aggregation node of the primary and backup CR-LSPs. It cannot be the ingress of the primary CR-LSP.
FRR is classified into the following types by protected object:
  Link protection: A PLR and an MP are directly connected. A bypass CR-LSP only protects the direct link to the PLR.
  Node protection: A PLR and an MP are indirectly connected. A bypass CR-LSP protects a direct link to the PLR and nodes on the primary CR-LSP's path between the PLR and MP.
Notes: The bypass CR-LSP mentioned here is a local backup CR-LSP created by FRR, not a backup CR-LSP created in path protection.
If node protection is enabled, only the link between the protected node and PLR is protected. The PLR cannot detect faults in the link between the protected node and the MP.

## Slide 75: Related FRR Concepts (2)
R1
R2
R3
R4
R5
R6
R7
R8
Primary CR-LSP
Backup CR-LSP1
Backup CR-LSP2
PLR
MP
MP
R2 is the PLR of the primary tunnel.
R3 is the MP of backup CR-LSP1, and R4 is the MP of backup CR-LSP2.
Backup CR-LSP1 provides link protection for the primary CR-LSP.
Backup CR-LSP2 provides node protection for the primary CR-LSP.
R3 is the next hop (NHOP) router of the PLR.
R4 is the next-next hop (NNHOP) router of the PLR
Protected link
Protected node
Notes: NHOP router: PLR's next hop router of the primary CR-LSP.
NNHOP router: PLR's next-next hop router of the primary CR-LSP.
The PLR of the primary CR-LSP already knows the NHOP and NNHOP. Link protection can be provided if the egress LSR ID of the bypass CR-LSP is the same as the NHOP LSR ID. Node protection can be provided if the egress LSR ID of the bypass CR-LSP is the same as the NNHOP LSR ID.
When a link fault is detected, traffic is switched to the protection link within 50 ms. At the same time, the ingress of the primary tunnel is notified to re-optimize the primary tunnel.
Link protection protects the link from PLR to MP (NHOP) instead of a specific LSP. Therefore, the bypass tunnel can protect multiple LSPs.
Link protection works in one-to-many mode. Therefore, switching may cause partial congestion on the network.

## Slide 76: Protection Modes Supported by FRR (1)
One-to-one backup
  A detour CR-LSP is automatically set up on each eligible node along each primary CR-LSP to protect downstream links or nodes.
  CR-LSPs are used to protect CR-LSPs. The primary and backup CR-LSPs belong to the same tunnel.
  In one-to-one backup mode, packets are forwarded with only one label.
Primary CR-LSP
R1
R2
R5
R6
R3
R4
PLR
PLR
MP
Detour CR-LSP 1
Detour CR-LSP 2
Notes: Detour CR-LSP: A detour LSP is automatically established on each node along the primary CR-LSP. Detour LSPs and the primary CR-LSP are in the same tunnel.
This mode is easy to configure, eliminates manual network planning, and provides flexibility on a complex network. However, this mode has low extensibility, requires maintenance of the backup CR-LSP status on each node, and consumes more bandwidth than the facility backup mode.

## Slide 77: Protection Modes Supported by FRR (2)
Facility backup
  A bypass tunnel is configured for each link or node that may fail on a primary tunnel. A bypass tunnel can protect traffic on multiple primary tunnels.
  The primary and backup LSPs belong to different TE tunnels.
  The facility backup mode requires two layers of labels during forwarding and supports label nesting.
Currently, mainstream vendors in the industry usually adopt the facility backup mode.
Primary CR-LSP
Bypass CR-LSP 1
R1
R2
R5
R6
R3
R4
PLR
MP
Notes: A bypass CR-LSP can protect multiple primary CR-LSPs. The bypass and primary CR-LSPs are established in different tunnels.
This mode is extensible, resource efficient, and easy to implement. However, bypass tunnels must be manually planned and configured, which is time-consuming and labor-intensive on a complex network.

## Slide 78: TE FRR Implementation
Facility backup mode:
  A bypass CR-LSP can be configured in manual or automatic mode. In automatic mode, a node enabled with auto FRR automatically establishes a bypass CR-LSP and binds it to the primary CR-LSP as long as the primary CR-LSP that passes through the node sends an FRR protection request and the topology meets the requirements of the FRR topology.
  You can determine whether to configure bandwidth values for bypass CR-LSPs based on actual situations to implement bandwidth protection.
One-to-one backup mode:
  Detour CR-LSPs are automatically established on each node and do not need to be manually configured.
  By default, a detour LSP has the same bandwidth as the primary CR-LSP and automatically provides bandwidth protection.

## Slide 79: Implementation of TE FRR
The following uses the facility backup mode as an example. The procedure is as follows:
  Establish the primary and backup CR-LSPs.
  Bind a bypass CR-LSP to the primary CR-LSP.
  Perform fault detection.
  Perform traffic switching.
  Perform a switchback.

## Slide 80: Setting up a Primary CR-LSP
The process of setting up a primary CR-LSP is similar to that of setting up a common CR-LSP. The difference lies in that the ingress adds flags such as Local Protection desired and Label Record desired to the Session_Attribute object in a Path message during the setup of the primary CR-LSP. If bandwidth protection is required, a "bandwidth protection desired" flag is added to the Path message.
R1
R2
R3
R4
R5
Path
Resv
<R1> display mpls rsvp-te psb-content
-------------------------------------------------------------------------------
The PSB Content
-------------------------------------------------------------------------------
Tunnel Addr: 5.5.5.5 Exist time: 16h 1m 13s
Tunnel ExtID: 1.1.1.1 Session ID: 100
Session Attribute:
SetupPrio: 7 HoldPrio: 7
SessionAttrib: SE Style desired
Label Record desired //Indicates that label recording is required.
Local Protection desired //Indicates that FRR protection is required.
Bandwidth Protection desired //Indicates that bandwidth protection is required.
POP
101
100
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: To obtain the label allocated by the NNHOP to the NHOP node, set the Label Recording Desired value in the Session_Attribute object of the Path message to 0x02.

## Slide 81: Backup CR-LSP Setup
For the facility backup mode:
  In manual mode, you need to manually configure a bypass CR-LSP on the PLR.
  In automatic mode, you need to enable auto FRR on the PLR, which then automatically creates a bypass CR-LSP based on the network topology.
R1
R2
R3
R4
R5
Bypass CR-LSP
PLR
MP
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs

## Slide 82: Bypass CR-LSP Binding
The process of searching for a suitable bypass CR-LSP is called bypass CR-LSP binding. Only the primary CR-LSP with the "local protection desired" flag can trigger a binding process. The binding must be complete before a primary/bypass CR-LSP switchover is performed.
The "local protection desired" flag is configured on the ingress of the primary CR-LSP.
PLR
NHP
NNHOP
Bypass CR-LSP 1
Link protection
Bypass CR-LSP 2
Node protection
Primary CR-LSP
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: The process of searching for a suitable bypass CR-LSP is called bypass CR-LSP binding. Only the primary CR-LSP with the "local protection desired" flag can trigger a binding process. The binding must be complete before a primary/bypass CR-LSP switchover is performed. During the binding, the PLR must obtain information about the outbound interface of the bypass CR-LSP, next hop label forwarding entry (NHLFE), LSR ID of the MP, label allocated by the MP, and protection type.
The PLR of the primary CR-LSP already knows the NHOP and NNHOP. Link protection can be provided if the egress LSR ID of the bypass CR-LSP is the same as the NHOP LSR ID. Node protection can be provided if the egress LSR ID of the bypass CR-LSP is the same as the NNHOP LSR ID. For example, in the preceding figure, bypass CR-LSP 1 protects a link, and bypass CR-LSP 2 protects a node.
After a bypass CR-LSP is successfully bound to the primary CR-LSP, the NHLFE of the primary CR-LSP is recorded. The NHLFE contains the NHLFE index of the bypass CR-LSP and the inner label assigned by the MP. The inner label is used to forward traffic during FRR switching.

## Slide 83: Fault Detection
Currently, the following fault detection mechanisms are available:
  Failure detection mechanism for a specific physical layer, such as SDH/SONET APS
  Keepalive detection for P2P links such as PPP and HDLC links
  RSVP-TE extended Hello packets (manually enabled on the interface)
  BFD
  MPLS operation, administration and maintenance (OAM)
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: BFD is a new fault detection mechanism that can be used to detect the reachability of vairous routing protocols (OSPF/IS-IS/BGP), MPLS LSP, VOIP, WG, and various upper-layer (for example, application layer) connections to speed up convergence.
MPLS OAM can also quickly detect MPLS LSP faults and complete traffic switching within 50 ms.
If node protection is enabled, only the link between the protected node and PLR is protected. The PLR cannot detect faults in the link between the protected node and the MP.

## Slide 84: Traffic Switching
The PLR switches traffic to the backup CR-LSP upon detection of a link failure. The internal processing of the PLR is as follows:
  Ensure that the backup CR-LSP is ready and the label allocated to the backup tunnel is ready.
  Traffic is switched to the backup CR-LSP after the preceding step is complete. During the switching, the corresponding parameters in the RSVP packets are modified or updated:
    Clear the Local Protection Desired flag in the Session_Attribute object.
    Change the IP address of the outbound interface on the PLR to the IP address of the outbound interface on the backup CR-LSP.
    Generate a new ERO.
    Update the RRO.
    Change PLR labels — two-Layer label nesting
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs

## Slide 85: Packet Forwarding Before TE FRR Switching
1024
IP
1025
IP
1022
IP
Swap
Swap
Primary CR-LSP
Bypass CR-LSP
IP
Pop
PLR
MP
R1
R2
R3
R4
R7
R5
R6
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: Before TE FRR switching is performed, traffic is forwarded along the primary CR-LSP, and labels are pushed in and popped out along the primary CR-LSP.

## Slide 86: Packet Forwarding After TE FRR Switching
34
1022
IP
IP
Pop 35
Swap 1024–1022
Push 34
35
1022
IP
1022
IP
1024
IP
Swap
Pop 1022
PLR
MP
R1
R2
R3
R4
R7
R5
R6
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: If a primary CR-LSP fails, the PLR switches both service traffic and RSVP messages to a bypass CR-LSP and advertises the switchover event upstream. During the switchover, the MPLS label nesting mechanism is used. The PLR pushes the inner and outer labels that the MP assigns for the primary and bypass CR-LSPs, respectively. The penultimate hop along the bypass CR-LSP removes the outer label from the packet and forwards the packet only with the inner label to the MP. The MP forwards the packet to the next hop along the primary CR-LSP.
The bypass CR-LSP provides node protection. If R3 or the link between R2 and R3 fails, traffic is switched to the bypass CR-LSP. During the switching, the PLR (R2) swaps an inner label 1024 for an inner label 1022, pushes an outer label 34 into the packet, and forwards the packet over the bypass CR-LSP. After the packet arrives at R4, the R4 forwards the packet to the next hop. The packet finally arrives at the tunnel egress.

## Slide 87: Signaling Process After a Fault Occurs - Local Protection Not Configured
After a link or node fails, the upstream signaling process is as follows:
  The PLR sends a Path_Error message to the ingress and disables the primary LSP.
After a link or node fails, the downstream signaling process is as follows:
  If local protection is not configured, the MP sends a Path_Tear message downstream to tear down the primary LSP if it does not receive Path information from upstream within a period of time.
ResvTear
PathTear
ResvTear
PathTear
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: If local protection is not configured, the PLR immediately sends a Path_Error message upstream and disables the primary LSP. If the MP does not receive a Path message upstream after a period of time, the MP sends a Path_Tear message downstream to delete the local state created by each node. Upon receipt, each node sends a ResvTear message upstream to delete the corresponding local resources.

## Slide 88: Signaling Process After a Link Fails - After Local Protection Is Configured (1)
After a link or node fails, the upstream signaling process is as follows:
  A Path_Error message carries an extended object to notify the upstream node that local protection has been enabled for the primary LSP. In this case, path recomputation rather than LSP teardown is required. After a new LSP is established along the calculated optimal path, traffic is switched to the new path for forwarding.
After a link or node fails, the downstream signaling process is as follows:
  The PLR sends Path messages along the backup LSP for each protected LSP to ensure that the primary LSP is not torn down. In addition, the MP periodically sends Path messages downstream to maintain the soft states of the entire LSP.
IGP notification process: On an MPLS TE network, if a link fails, both IGP and RSVP advertise the link failure status. The ingress of a tunnel ignores link failure notifications from an IGP to prevent the LSP from being deleted due to IGP notifications.
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: Upstream signaling process: The original Path_Error message is extended by adding Code=25 (Notification) and Subcode=3 (Tunnel locally repaired). This indicates that local protection has been enabled for the primary LSP and that path recalculation rather than LSP teardown is required. After a new LSP is set up along the optimal path, traffic is switched to the new path for forwarding.

## Slide 89: Signaling Process After a Link Fails - After Local Protection Is Configured (2)
PLR
MP
R1
R2
R3
R4
R7
PathErr
Local protection is enabled on the primary CR-LSP, which remains in the Up state.
Path
Path
Path
Path
Waits for the MP to send Path information and
maintains the soft state of the CR-LSP.
Bypass CR-LSP
Primary CR-LSP
Bypass CR-LSP
1
2
3
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: The upstream node is notified that local protection is enabled for the primary LSP and LSP teardown is not required. Step 1
The PLR sends Path messages along the bypass LSP for each protected LSP to ensure that the primary LSP is not torn down. Step 2
The MP periodically sends Path messages downstream to maintain the soft states of the entire LSP. Step 3

## Slide 90: Traffic Switchback After the Fault Is Rectified
After TE FRR (including auto FRR) switching is complete, the ingress of the primary CR-LSP attempts to reestablish the primary CR-LSP using the make-before-break mechanism. Service traffic and RSVP messages then switch from the bypass CR-LSP back to the successfully reestablished primary CR-LSP. The reestablished CR-LSP is called a modified CR-LSP.
Modified CR-LSP
Bypass CR-LSP
MP
PLR
Bypass CR-LSP Binding
Fault Detection
Switchover
Switchback
Setup of Primary and Backup CR-LSPs
Notes: For an established MPLS TE tunnel, topology and resource changes may cause the original LSP to fail to meet the requirements. This means that a new CR-LSP needs to be established. If traffic is switched to the new CR-LSP before it is established, as a result, traffic loss may occur.
Make-before-break is a mechanism that allows a CR-LSP to be established using changed MPLS TE tunnel attributes (such as bandwidth and path) over a new path before the original CR-LSP is torn down. It helps minimize data loss and additional bandwidth consumption. The new CR-LSP is called a modified CR-LSP. Make-before-break is implemented using the shared explicit (SE) resource reservation style.
The new CR-LSP may compete with the primary CR-LSP on some shared links for bandwidth. The new CR-LSP cannot be established if it fails the competition. The make-before-break mechanism allows the new CR-LSP to use the bandwidth of the original path, without needing to recalculate the bandwidth to be reserved for the new path. Additional bandwidth resources are consumed only when some links on the new LSP do not overlap with those on the original LSP.

## Slide 91: Joint Use of Path Protection and FRR (1)
When hot standby and TE FRR are used together, the PLR location varies according to the fault location. Accordingly, the switching sequences of CR-LSP hot standby and TE FRR are different.
  If the PLR is the ingress of the primary CR-LSP, it can fast detect the fault and immediately switch traffic to the hot-standby CR-LSP instead of entering the TE FRR process.
  If the PLR is a transit node along the primary CR-LSP, the ingress of the primary CR-LSP may fail to detect the fault in time. To ensure uninterrupted traffic forwarding, the PLR switches traffic to the TE FRR bypass tunnel before transmitting the fault information to the ingress of the primary CR-LSP through RSVP signaling, triggering the ingress to switch traffic to the hot-standby CR-LSP.
Notes: TE FRR is a temporary local protection mechanism used when the ingress does not detect a fault. It is a supplement to CR-LSP hot standby. Once the ingress of the primary CR-LSP detects the fault, it switches traffic to the hot-standby CR-LSP.
If the PLR is a transit node along the primary CR-LSP, the ingress cannot quickly detect the fault due to slow RSVP signaling transmission. As a result, traffic is always forwarded over the TE FRR bypass tunnel. To speed up switching of traffic to the hot-standby CR-LSP by the ingress, you can enable CSPF fast switching. After this function is enabled, an IGP notifies the ingress of the primary CR-LSP when its topology changes. After detecting the fault, the ingress of the primary CR-LSP does not wait for RSVP signaling but switches traffic to the hot-standby CR-LSP in advance.
If the hot-standby CR-LSP is down, the ingress keeps attempting to reestablish a hot-standby CR-LSP.

## Slide 92: Joint Use of Path Protection and FRR (2)
If ordinary backup and TE FRR are used together:
  If ordinary backup is not associated with TE FRR: If a protected link or node fails, a PLR switches traffic to a bypass CR-LSP. Only after both the primary and bypass CR-LSPs fail, the ingress of the primary CR-LSP attempts to establish an ordinary backup CR-LSP and switches traffic to this CR-LSP.
  If ordinary backup is associated with TE FRR: If a protected link or node fails, a PLR switches traffic to a bypass CR-LSP first. If the PLR is the ingress of the primary CR-LSP, the PLR attempts to set up an ordinary backup CR-LSP. After the ordinary backup CR-LSP is set up, the PLR switches traffic to this CR-LSP. If the PLR is a transit node on the primary CR-LSP, the PLR uses RSVP signaling to send fault information to the ingress of the primary CR-LSP, triggering the ingress to attempt to set up an ordinary backup CR-LSP. If the ordinary backup CR-LSP is set up successfully, the ingress switches traffic to this CR-LSP.

## Slide 93: SRLG
Shared risk link group (SRLG) is a constraint used for hot-standby tunnel path computation in CR-LSP hot standby and TE FRR scenarios. This constraint can prevent the primary and hot-standby paths of a tunnel from traveling on links with the same risk level, further enhancing TE tunnel reliability.
As shown in the logical topology, the primary CR-LSP is established over the path PE1 → P1 → P2 → PE2. The link between P1 and P2 is protected by an FRR bypass tunnel established over the path P1 → P3 → P2.
In actual networking, the core nodes (P1, P2, and P3) of the backbone network are connected through devices of the transport network. In network deployment, the core nodes may often share the links of the transport network. In this case, if the shared link fails, both the primary and FRR bypass tunnels are affected, causing FRR protection to fail. An SRLG can be configured to prevent the FRR bypass tunnel from sharing a link with the primary tunnel, ensuring that FRR or CR-LSP hot standby properly protects the primary CR-LSP.
PE1
PLR
MP
P1
P2
PE2
P3
Primary CR-LSP
Bypass CR-LSP
Logical topology
Physical topology
PE1
P1
P2
PE2
P3
Transmission
device
Shared links
SRLG
Notes: An SRLG is a set of links at the same risk of faults. If a link in an SRLG fails, other links may also fail. If a link in this group is used by a hot-standby CR-LSP or FRR bypass CR-LSP of the failed link, the hot-standby CR-LSP or FRR bypass CR-LSP cannot provide protection.
SRLG is a link attribute, in numerical notation. The links with the same SRLG value are in one SRLG.
IGP TE advertises SRLG information to all nodes in a single MPLS TE domain through an IGP. The CSPF algorithm uses the SRLG attribute together with other constraints, such as bandwidth, to calculate a path.
The MPLS TE SRLG works in either of the following modes:
  Strict mode: The SRLG attribute is a necessary constraint used by CSPF to calculate a path for a hot-standby CR-LSP or an FRR bypass CR-LSP.
  Preferred mode: The SRLG attribute is an optional constraint used by CSPF to calculate a path for a hot-standby CR-LSP or FRR bypass CR-LSP. For example, if CSPF fails to calculate a path for a hot-standby CR-LSP based on the SRLG attribute, CSPF recalculates the path without taking into account the SRLG attribute.

## Slide 94
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
  Path Protection
  Local Protection (FRR)
  MPLS TE Tunnel Protection Group
  Fault Detection
Advanced MPLS TE Features

## Slide 95: Tunnel Protection Group Overview
A tunnel protection group provides E2E protection for MPLS TE tunnels. If a working tunnel in a protection group fails, traffic switches to a protection tunnel, minimizing traffic interruptions.
The working and protection tunnels must be bidirectional. Therefore, an MPLS TE tunnel protection group supports associated bidirectional LSPs and static bidirectional co-routed LSPs.
As shown in the figure, Tunnel1 and Tunnel2 are working tunnels, and Tunnel3 and Tunnel4 are protection tunnels. The four tunnels form an MPLS TE tunnel protection group. When a fault is detected on a working tunnel, traffic is switched to a protection tunnel for forwarding.
Tunnel1
Tunnel2
Tunnel3
Tunnel4
Working tunnel
Protection tunnel

## Slide 96: Tunnel Protection Group Implementation (1)
Tunnel establishment: Bidirectional primary and protection tunnels are established. The tunnel establishment process is similar to the process of establishing a common TE tunnel. Note that the primary and protection tunnels must have the same ingress and destination IP address.
A protection tunnel cannot be protected by another protection tunnel, and TE FRR cannot be enabled for the protection tunnel.
Tunnel attribute inconsistency between the working and protection tunnels facilitates network planning.
Tunnel1
Tunnel2
Tunnel3
Tunnel4
Working tunnel
Protection tunnel
1. Tunnel establishment
R1
R5

## Slide 97: Tunnel Protection Group Implementation (2)
2. Binding of working and protection tunnels
3. Fault detection
[R1-tunnel1] mpls te tunnel-id 100
[R5-tunnel2] mpls te tunnel-id 200
[R1-tunnel3] mpls te tunnel-id 101
[R5-tunnel4] mpls te tunnel-id 201
[R1] interface tunnel 1
[R1-tunnel1] mpls te protection tunnel 101
[R5] interface tunnel 2
[R5-tunnel2] mpls te protection tunnel 201
After the tunnel protection group function is enabled for a working tunnel, the working tunnel and a protection tunnel are bound to form a tunnel protection group.
As shown below, a tunnel ID is set for each tunnel, and each protection tunnel with a specified tunnel ID is bound to a working tunnel.
MPLS OAM/MPLS-TP OAM is used to detect faults in a tunnel protection group to speed up protection switching.
As shown below, MPLS-TP OAM is configured on the ingress of the forward and reverse primary tunnels to detect faults.
[R1] mpls-tp meg abc
[R1-mpls-tp-meg-abc] me te interface Tunnel 1 mep-id 1 remote-mep-id 2
[R5] mpls-tp meg abc
[R5-mpls-tp-meg-abc] me te interface Tunnel 2 mep-id 2 remote-mep-id 1

## Slide 98: Tunnel Protection Group Implementation (3)
4. Protection switching
5. Switchback
[R1] interface tunnel 1
[R1-tunnel1] mpls te protection tunnel 101 mode revertive wtr 0
[R5] interface tunnel 2
[R5-tunnel2] mpls te protection tunnel 201 mode revertive wtr 0
When the ingress detects a fault on the working tunnel, it triggers protection switching in the tunnel protection group. Two modes are available:
  Manual switchover: A network administrator runs commands to switch traffic.
  Automatic switching: Automatic traffic switching is performed after the working tunnel detects a fault.
Currently, an MPLS TE tunnel protection group supports only bidirectional switching. That is, if a switchover is performed for traffic in one direction, a switchover is also performed for traffic in the opposite direction.
After a traffic switchover is complete, the ingress keeps trying to reestablish the working tunnel. If the working tunnel is reestablished, the ingress determines whether to switch traffic back to the working tunnel according to the configured switchback policy.
Configure the binding between the working and protection tunnels, specify whether to perform a switchback, and configured the WTR time:

## Slide 99: Differences Between CR-LSP Backup and a Tunnel Protection Group
Comparison Item | CR-LSP Backup | Tunnel Protection Group
Object to be protected | Primary and backup CR-LSPs are established on the same tunnel interface. The backup CR-LSP protects the primary CR-LSP. | In a tunnel protection group, one tunnel protects another.
TE FRR | TE FRR protection is supported only by the primary CP-LSP, not the backup CR-LSP. | A tunnel protection group depends on the reverse LSP, which is mutually exclusive with TE FRR. Therefore, tunnels in a tunnel protection group do not support TE FRR.
LSP attributes | The primary and backup CR-LSPs have the same attributes (such as bandwidth, setup priority, and hold priority), except for the TE FRR attribute. | Tunnels in a tunnel protection group use independent attributes. This means that attributes of one tunnel are irrelevant to those of another tunnel. For example, a protection tunnel without bandwidth can protect a working tunnel requiring bandwidth protection.

## Slide 100
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
  Path Protection
  Local Protection (FRR)
  MPLS TE Tunnel Protection Group
  Fault Detection
Advanced MPLS TE Features

## Slide 101: RSVP Hello
After a TE tunnel is established, Path and Resv messages are sent periodically to check neighbor reachability and to maintain the resource reservation status (including PSB and RSB) of nodes. This method, however, takes a long time. If a fault occurs on the primary path, traffic cannot be switched to the backup path in a timely manner. Therefore, RSVP Hello is introduced to solve this problem.
The RSVP Hello extension can rapidly monitor the reachability of RSVP nodes. If an RSVP node becomes unreachable, TE FRR protection is triggered.
Version | Flags | Message Type | RSVP Checksum
Send TTL |  | Reserved | RSVP Length
Object… |  |  | 
Type = 20 Hello
Notes: Hello messages are defined in RFC 3209 and used for fast detection (Keepalive) between MPLS TE neighbors.

## Slide 102: How RSVP Hello Works
Hello Request
Hello Ack
R1
R2
After RSVP Hello is enabled on R1, R1 sends a Hello Request message to R2. After receiving the message, R2 replies with a Hello ACK message. Upon receipt, R1 determines that its neighbor R2 is reachable.
R1
R2
Hello Request
Hello Request
Hello Request
If R2 does not respond Hello Ack messages to three consecutive Hello Request messages sent by R1, R1 triggers TE FRR switching, and re-initializes RSVP Hello.
Notes: R1 and R2 are connected through a direct link.

## Slide 103: BFD for TE CR-LSP (1)
As shown in the figure, the ingress of the tunnel cannot immediately detect a fault due to the Layer 2 switch. In this case, you can deploy the Hello protocol for fault detection, but the detection time is long. To resolve this problem, bind a BFD session to a CR-LSP. That is, set up a BFD session between the ingress and egress of a CR-LSP to solve the problem of long detection time. A BFD packet is sent by the ingress to the egress along the CR-LSP. Upon receipt, the egress responds to the BFD packet. The ingress can rapidly detect the status of links through which the CR-LSP passes.
After detecting a link fault, the ingress searches for a backup CR-LSP and switches traffic to the backup CR-LSP.
BFD for TE is usually used together with the hot-standby CR-LSP mechanism.
Notes: Conventional detection mechanisms such as RSVP Hello and RSVP Srefresh (summary refresh) mechanisms detect faults slowly. In contrast, BFD rapidly sends and receives packets to detect faults in a tunnel. If a fault occurs, BFD triggers rapid service switching to protect service traffic.

## Slide 104: BFD for TE CR-LSP (2)
Primary CR-LSP
Backup CR-LSP
BFD
BFD
A BFD session before a switchover
A BFD session after a switchover
Notes: A BFD session is set up to detect the link through which the primary LSP passes. If a fault occurs on this link, the BFD session on the ingress immediately reports the failure. The ingress switches traffic to the backup CR-LSP and sets up a new BFD session to detect faults on the link of the backup CR-LSP.

## Slide 105: BFD for RSVP
When a Layer 2 device exists on a link between two RSVP neighbors, BFD for RSVP can be deployed to rapidly detect faults in this link. If a link fault occurs, BFD for RSVP rapidly detects the fault and trigger TE FRR switching.
BFD for RSVP applies to the TE FRR networking where Layer 2 devices exist between the PLR and the RSVP neighbor along the primary CR-LSP.
R1
R2
R3
SW1
R4
R5
R6
Primary CR-LSP
BFD for RSVP
RSVP Hello
RSVP Hello
RSVP Hello
Bypass CR-LSP
Notes: When a Layer 2 device is deployed on the link between two neighboring RSVP nodes, the RSVP nodes can only use the Hello mechanism to detect link faults. As shown in the figure, a Layer 2 device (SW1) exists between R2 and R4. If the link between SW1 and R4 fails, R2 cannot quickly detect the fault through the link layer because SW1 isolates the fault. Instead, R2 can only be notified of the fault through the RSVP Hello mechanism. In this case, fault detection is performed in milliseconds, causing a large amount of data to be lost. BFD for RSVP can implement faster fault detection in this scenario, shorten the fault detection time, and trigger TE FRR to perform fast switchover, improving network reliability.

## Slide 106
Overview of MPLS TE
MPLS TE Fundamentals
MPLS TE Reliability
Advanced MPLS TE Features

## Slide 107: Tunnel Priority
MPLS TE tunnel priority:
  Eight priorities are provided. The value ranges from 0 to 7. A smaller value indicates a higher priority.
Tunnel priorities are classified into the following types:
  Setup priority
  Hold priority
Important services can preempt the resources of low-priority tunnels by setting high-priority tunnels to ensure service quality of high-end users.
If the setup priority of a new tunnel is higher than the hold priority of the original tunnel, tunnel preemption occurs.
R1
R2
Tunnel1
Tunnel2
[R1-Tunnel1] mpls te priority hold-priority 7
[R1-Tunnel2] mpls te priority setup-priority 6
Notes: As shown in the figure, the hold priority of Tunnel1 is lower than the setup priority of Tunnel2. When Tunnel2 needs to set up a tunnel on the link between R1 and R2 but the resources are insufficient, Tunnel2 preempts the resources of Tunnel1 to set up a tunnel, ensuring the normal running of high-priority services.

## Slide 108: Tunnel Preemption
The priority and preemption attributes are used in conjunction to determine resource preemption among tunnels. When multiple tunnels need to be set up, the tunnels with higher setup priorities preempt resources and are set up preferentially. If resources such as bandwidth are insufficient, a tunnel with a higher setup priority may preempt the bandwidth resources of an established tunnel with a lower hold priority.
MPLS TE supports the following tunnel preemption modes:
  Hard preemption: The original tunnel is directly torn down without being protected.
  Soft preemption: The original tunnel is not torn down, and a new tunnel is established. After traffic is switched, the original tunnel is torn down.
Notes: To prevent some tunnels from being preempted, you can set the setup priority to 7 and hold priority to 0.

## Slide 109: Tunnel Preemption Instance (1)
Tunnel1: R1 -> R3 -> R6. The required bandwidth is 155 Mbit/s, and the setup and hold priorities are both 0.
Tunnel2: R2 -> R3 -> R5. The required bandwidth is 155 Mbit/s, and the setup and hold priorities are both 7.
R1
R2
R3
R4
R5
R6
Tunnel1
Tunnel2
155 M
155 M
155 M
155 M
155 M
155 M
1000 M
Notes: Two TE tunnels with different priorities are set up. The priority of Tunnel1 is 0 and that of Tunnel2 is 7.

## Slide 110: Tunnel Preemption Instance (2)
When the link between R3 and R6 fails, R3 sends a ResvTear message to R1. R1 recalculates a new path R1 -> R3 -> R5 -> R6 for Tunnel1.
As shown in the figure, the bandwidth (155 Mbit/s) of the link between R3 and R5 is insufficient for Tunnel1 and Tunnel2 (310 Mbit/s in total). In this case, preemption occurs.
R1
R2
R3
R4
R5
R6
ResvTear
Tunnel1
Tunnel2

## Slide 111: Tunnel Preemption Mode - Hard Preemption
In hard preemption mode, R3 directly sends an RSVP message to tear down Tunnel2 because Tunnel1 has a higher priority than Tunnel2.
In hard preemption mode, if Tunnel2 has traffic, some traffic will be lost.
R1
R2
R3
R4
R5
R6
ResvTear
Tunnel1
Tunnel2
Notes: Hard preemption: When a high-priority tunnel competes for resources with a low-priority tunnel, the high-priority tunnel directly preempts resources of the low-priority tunnel without waiting. As a result, some traffic is lost.

## Slide 112: Tunnel Preemption Mode - Soft Preemption
In soft preemption mode, R3 sends a Resv message to R2 and sets Preemption pending in the message.
In make-before-break mode, Tunnel2 is re-established along the path R2 -> R4 -> R6 -> R5 without tearing down Tunnel2 on R2. The original Tunnel 2 is torn down after traffic switching is complete.
R1
R2
R3
R4
R5
R6
Resv
Tunnel1
Tunnel2
Modified Tunnel2
Notes: Soft preemption: The make-before-break mechanism applies. A CR-LSP with a higher priority has to wait until traffic over a lower-priority CR-LSP switches to another CR-LSP before the higher-priority CR-LSP preempts bandwidth assigned to the lower-priority CR-LSP.

## Slide 113: Tunnel Re-optimization
After a CR-LSP is established in a tunnel, the path of the CR-LSP can be optimized based on changes in bandwidth, traffic requirements, management policies, and other factors of the network.
A CR-LSP can be optimized when a better path is available. That is, the CR-LSP is re-set up only when a better path with a smaller metric and fewer hops exists.
Tunnel optimization uses the make-before-break mechanism to ensure user service continuity.
During tunnel re-optimization, the share explicit (SE) mode must be used to prevent overlapping of the old and new CR-LSPs.
Re-optimization is classified into the following modes by triggering mode:
  Automatic re-optimization: enables an ingress to run CSPF to calculate a path for a CR-LSP after a configured re-optimization triggering interval elapses. If CSPF calculates a path with a metric value smaller than that of the existing path, the CR-LSP is reestablished over the better path. If the CR-LSP is successfully established, the system notifies the forwarding plane to switch traffic and tear down the original CR-LSP. After the process, re-optimization is complete. If the CR-LSP fails to be reestablished, traffic still travels through the original CR-LSP.
  Manual re-optimization: A network administrator runs a re-optimization command in the user view to trigger path re-optimization on the ingress.
Notes: In some special circumstances, TE tunnel re-optimization is not desired. MPLS TE provides the tunnel locking function. If this function is enabled for a tunnel, the tunnel cannot be re-optimized after being established.
If the tunnel uses the fixed filter (FF) reservation style, tunnel re-optimization cannot be configured.
Although re-optimization can be successfully configured for TE tunnels established over explicit paths, the configuration does not take effect.

## Slide 114: Re-optimization of Tunnels in SE Mode
Originally, R1 notifies the network of the 35 Mbit/s bandwidth request, and the path selected by the tunnel is R1 -> R3 -> R4.
The original bandwidth needs to be increased to 80 Mbit/s to meet new service requirements. If the original link bandwidth cannot meet the requirements, the ingress of the tunnel recalculates a tunnel path and selects the path R1 -> R2 -> R3 ->R4.
The make-before-break mechanism is adopted. The total bandwidth required on the path between R3 and R4 will exceed 100 Mbit/s.
The SE mode ensures that the old and new LSPs share bandwidth resources on the path between R3 and R4 until the old tunnel is torn down.
R4
R3
R2
R1
35 M
80 M
80 M
100 M
80 Mbit/s ＋ 35 Mbit/s > 100 Mbit/s
Notes: The SE mode is an important condition for implementing the make-before-break mechanism.
In SE mode, bandwidth resources can be shared only in the same session.

## Slide 115: Automatic Bandwidth Adjustment
The bandwidth change diagram within a sampling period can be obtained by periodically (sampling frequency) sampling traffic of each LSP.
The highest sampling bandwidth can be obtained within a sampling period. Then, the highest sampling bandwidth is used as the tunnel bandwidth to initiate the establishment of a new LSP.
After the LSP is established, traffic switches to this LSP and the original LSP is torn down.
If the LSP fails to be established, traffic is still transmitted along the original LSP. Traffic is adjusted again after the net sampling period elapses.
To avoid unnecessary adjustments, you can configure an adjustment threshold. The bandwidth is adjusted only when the ratio of the maximum sampling bandwidth of this time to the maximum sampling bandwidth of last time reaches a certain threshold.

## Slide 116: Automatic Bandwidth Adjustment
Bandwidth
Time
T1
T2
T3
BW1
BW2
BW3
T0
T4
Notes: The maximum sampling bandwidth BW1 is obtained in the time range from T0 to T1, and a new LSP uses BW1 as the reserved bandwidth in the time range from T1 to T2.
The maximum sampling bandwidth BW2 is obtained in the time range from T1 to T2, and a new LSP uses BW2 as the reserved bandwidth in the time range from T2 to T3.
The maximum sampling bandwidth BW3 is obtained in the time range from T2 to T3, and a new LSP uses BW3 as the reserved bandwidth in the time range from T3 to T4.

## Slide 117: Load Balancing (1)
Traditional IP routing protocols support equal-cost load balancing and unequal-cost load balancing. Load balancing is determined by the characteristics of routing protocols.
MPLS TE tunnels also support equal-cost and unequal-cost load balancing.
  Equal-cost load balancing mode: Similar to IP load balancing, per-packet load balancing or per-flow load balancing can be used. Generally, the per-flow mode is used.
  Unequal-cost load balancing mode:
    Traffic is load balanced based on the bandwidth ratio configured for each tunnel.
    Traffic is load balanced based on the configured load balancing value.
Note: Load balancing is not supported between TE tunnels and IGP routes. Traffic can be load balanced only by establishing multiple TE tunnels to the destination.
Notes: Unequal-cost load balancing supports EIGRP.
Equal-cost load balancing supports the following routing protocols: OSPF and IS-IS

## Slide 118: Load Balancing (2)
Traffic load balancing can be implemented by establishing two tunnels with the same destination address and reserved resources on the ingress of a tunnel.
R1
R2
R3
R4
R5
R6
Tunnel1
Tunnel2
Notes: In most cases, the requirements differ from the actual situation. Therefore, after a TE tunnel is established, you need to monitor the traffic of the TE tunnel and adjust the reserved bandwidth of the tunnel in real time to ensure that network resources are properly used.

## Slide 119
(Multiple-answer question) In which of the following situations does MPLS TE advertise link information? ( )
  A link is activated or deactivated.
  The link bandwidth changes.
  The administrative group attribute of an interface changes.
  The affinity attribute of a tunnel changes.
(Multiple-answer question) After an MPLS TE tunnel is successfully established, which of the following methods can be used to import traffic to the tunnel? ( )
  Static route
  Auto route
  PBR
  Tunnel policy
Notes: ABC
ABCD

## Slide 120
MPLS TE establishes CR-LSPs and directs traffic to these LSPs for transparent transmission. In this manner, network traffic is transmitted along specified paths, achieving traffic engineering. MPLS TE uses the information advertisement component, path computation component, and path establishment component to establish an E2E MPLS TE tunnel. Then, the traffic forwarding component directs service traffic to the tunnel to complete forwarding of service traffic.
MPLS TE supports multiple detection and protection mechanisms, such as TE FRR, CR-LSP backup, tunnel protection group, BFD for CR-LSP, and BFD for RSVP. If an MPLS TE tunnel fails or a node on the network is congested, the failure or congestion can be quickly detected and traffic can be switched to a backup path.
This course describes the working principles, tunnel protection, fault detection, and some advanced features of MPLS TE, which lays a foundation for the subsequent study of segment routing.