## Slide 1
Datacom
V5R2
V1.0
He Junjian/wx580230
2021.2.22
Liu Shuying/00245623, Wang Qiusheng/00287740,
New
He Junjian/wx580230
2021.6.07
Wan Changli/wx408647, Zhu Shigeng/00261992
Update

## Slide 2: SRv6 Overview

## Slide 3
At the beginning of the Segment Routing (SR) architecture design, two implementation modes were designed for the data plane. One is Segment Routing-Multiprotocol Label Switching (SR-MPLS), which reuses the MPLS data plane and can be incrementally deployed on the existing IP/MPLS network. The other is Segment Routing IPv6 (SRv6), which uses the IPv6 data plane and implements extension based on the IPv6 Routing header.
This document describes the concepts and fundamentals of SRv6 and its applications for Huawei NetEngine series routers.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the background of SRv6.
  Describe the technical advantages of SRv6.
  Describe the concepts and fundamentals of SRv6.
  Understand how to configure SRv6 BE and static SRv6 Policies.

## Slide 5
SRv6 Overview
SRv6 Network Programming
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 6: IP/MPLS Network Introduction
As a Layer 2.5 technology that runs between Layer 2 and Layer 3, MPLS adds connection-oriented attributes to connectionless IP networks. Traditional MPLS label-based forwarding improves the forwarding efficiency of IP networks. However, as hardware capabilities continue to improve, MPLS no longer features distinct advantages in forwarding efficiency. Nevertheless, MPLS provides good QoS guarantee for IP networks through connection-oriented label forwarding and also supports TE, VPN, and FRR.
IP/MPLS networks have gradually replaced dedicated networks, such as ATM, frame relay (FR), and X.25. Ultimately, MPLS is applied to various networks, including IP backbone, metro, and mobile transport, to support multi-service transport and implement the Internet's all-IP transformation.
IP header-based forwarding
MPLS label-based forwarding
MPLS label-based forwarding
IP header-based forwarding
IP network
IP network
3.3.3.0/24
IP
packet
MPLS
header
Ethernet
header
Destination: 3.3.3.3
IP/MPLS network
Notes: In the initial stage of network development, multiple types of networks, such as X.25, FR, ATM, and IP, co-existed to meet different service requirements. These networks could not interwork with each other, and on top of that, also competed, with mainly ATM and IP networks taking center stage. ATM is a transmission mode that uses fixed-length cell switching. It establishes paths in connection-oriented mode, and can provide better QoS capabilities than IP. Its design philosophy involves centering on networks and providing reliable transmission, and its design concepts reflect the reliability and manageability requirements of telecommunications networks. This is the reason why ATM was widely deployed on early telecommunications networks. The design concepts of IP differ greatly from those of ATM. To be more precise, IP is a connectionless communication mechanism that provides the best-effort forwarding capability, and the packet length is not fixed. On top of that, IP networks mainly rely on the transport-layer protocols (e.g., TCP) to ensure transmission reliability, and the requirement for the network layer involves ease of use. The design concept of IP networks embodies the "terminal-centric and best-effort" notion of the computer network, enabling IP to meet the computer network's service requirements. The competition between the two can essentially be represented as a competition between telecommunications and computer networks. As the network scale expanded and network services increased in number, ATM networks became more complex than IP networks, while also bearing higher management costs. Within the context of costs versus benefits for telecom carriers, ATM networks were gradually replaced by IP networks.
Although IP is more suitable for the development of computer networks than ATM, computer networks require a certain level of QoS guarantee. To compensate for the IP network's insufficient QoS capabilities, numerous technologies integrating IP and ATM, such as local area network emulation (LANE) and IP over ATM (IPoA), have been proposed. However, these technologies only addressed part of the issue, until 1996 when MPLS technology was proposed to provide a better solution to this issue.

## Slide 7: SR Origin and Solution
The SDN concept has a great impact on the network industry, and many protocols used for SDN implementation emerge in the industry, including OpenFlow, Protocol Oblivious Forwarding (POF), Programming Protocol-independent Packet Processors (P4), and SR. Compared with revolutionary protocols, SR considers compatibility with the existing network and smooth evolution, and also provides programmability. It is a de facto SDN standard.
  Advantages
  Disadvantages
SRv6
Extension based on the IPv6 Routing header
SR-MPLS
Incremental deployment on the existing IP/MPLS network
  Solutions
IP
LDP
RSVP-TE
ECMP
Label-based forwarding
Bandwidth reservation
Path planning
Lack of the path planning capability
Complex configuration/maintenance
Lack of the load balancing capability
No support for large-scale deployment
LDP-IGP synchronization issue
Simple configuration
Notes: SR resolves many issues on IP/MPLS networks through two solutions: SR-MPLS (based on MPLS forwarding) and SRv6 (based on IPv6 forwarding).

## Slide 8: From MPLS to SRv6
MPLS causes isolated network islands. SRv6 provides a unified forwarding plane and has advantages such as simplified protocols, high scalability, and programmability.
Forwarding plane
Control plane
Classic MPLS
SR-MPLS
LDP
RSVP-TE
IGP
IGP + SR extension
Payload
Payload
MPLS 1949
Payload
MPLS 1949
Payload
Push
Swap
Pop
Payload
Payload
MPLS 222
Payload
Payload
Push
Continue
Next
SRv6
IGP + SR extension
Payload
Payload
IPv6 + SRH
Payload
Payload
IPv6 + SRH
MPLS 111
MPLS 111
MPLS 2004
MPLS 1368
Control plane simplification
Forwarding plane simplification
Simplified protocols
High scalability
Programmability
Notes: Although MPLS plays an important role in the all-IP transformation of networks, it causes isolated network islands. On the one hand, it increases the complexity of cross-domain network interconnection. For example, solutions such as the MPLS VPN Option A/B/C solution are complex to deploy and involve difficult E2E service deployment. On the other hand, as the Internet and cloud computing develop, more and more cloud data centers are built. To meet tenants' networking requirements, multiple overlay technologies have been proposed, among which VXLAN is a typical example. In the past, quite a few attempts were made to provide VPN services by introducing MPLS to data centers. However, these attempts all wound up in failure due to multiple factors, including numerous network boundaries, complex management, and insufficient scalability. As such, the traffic from an end user to a service in a data center may typically need to pass through the VLAN, IP network, IP/MPLS network, and VXLAN network.
The combination of MPLS and SR is intended to provide programmability for networks as a practice of SDN implementation. However, this cannot satisfy services (such as SFC and IOAM) that need to carry metadata, as MPLS encapsulation has poor scalability. Nowadays, the IPv4 address space is almost exhausted. IPv6 and SR are combined, promoting the advent of SRv6.

## Slide 9: SRv6: Service-driven Network
Both SR-MPLS and SRv6 support the use of explicit paths defined on the ingress to guide traffic forwarding. Their overall architectures are the same.
Explicit paths established based on constraints, such as bandwidth, latency, and packet loss rate, can meet the requirements of different services.
Data download
Video
Voice
High bandwidth
Low latency
Low packet loss rate
NETCONF/BGP-LS/BGP IPv6 SR Policy
High-bandwidth path
Low-latency path
Low-packet-loss-rate path
Controller
Ingress
Notes: The biggest advantage of SRv6 over SR-MPLS is that IPv6 offers stronger network programming capabilities. Although IPv4 packets also contain a programmable Option field, this field can be used only in scenarios such as fault locating. IPv6, however, takes the extensibility of packet headers into account from the very beginning. Multiple extension headers, including Hop-by-Hop Options, Destination Options, and Routing headers, were designed to support further extension.
As of now, SRv6 network programming has grown rapidly, and SRv6 has been commercially deployed on multiple networks since the draft draft-ietf-spring-srv6-network-programming was proposed in 2019.

## Slide 10: Value and Significance of SR
MPLS is essentially an extension of IP functions and uses the shim mode to implement various flexible services. SRv6 integrates IP and MPLS functions, complying with the trend of technology development.
During the development of SDN, there was too much emphasis on the building of SDN controller capabilities, but the impact of network infrastructure on SDN controller capabilities was ignored. SRv6 greatly reduces bearer network complexity.
In the 5G and cloud era, more requirements are imposed on networks, such as stronger SLA assurance and deterministic latency. Network connection attributes are enhanced, and packets are required to carry more information. SRv6 extension can perfectly meet these requirements.

## Slide 11
SRv6 Overview
SRv6 Network Programming
  SRv6 Network Programming Overview
  SRv6 Segments & SRv6 Nodes
  SRv6 Instruction Sets
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 12: SRv6 Standards/Drafts
RFC 8402 (Segment Routing Architecture) introduces the source routing model through which the ingress controls traffic steering and forwarding by encapsulating an ordered list of segments. This behavior can be considered as specifying an ordered list of instructions on the ingress, with each instruction representing a function to be executed at a specific network location. Each function is locally defined on a node, for example, instructing the node to perform simple forwarding based on the corresponding segment list or to implement complex user-defined behaviors.
With greater focus on network programming, SRv6 (draft-ietf-spring-srv6-network-programming) combines simple and complex network functions to implement more network functions other than performing only forwarding. This draft defines the SRv6 network programming concept and main SR behaviors, such as SRv6 SIDs, SR endpoint behaviors, and SR Policy headend behaviors.
Notes: The following terms in this document are defined in RFC 8402: Segment Routing, SR domain, segment ID (SID), SRv6, SRv6 SID, SR Policy, prefix-SID, and Adj-SID.
The following terms in this document are defined in RFC 8754: SRH, SR source node, transit node, SR segment endpoint node, reduced SRH, Segments Left, and Last Entry.

## Slide 13: Introduction to Network Programming
Network programming stems from computer programming. In computer programming, we can convert our intent into a series of instructions that computers can understand and execute to meet our requirements. Similarly, if a network can work as a computer to translate the network intent into a series of forwarding instructions to be executed by network devices, network programming can be achieved.
Based on the preceding assumption, SRv6 was introduced to translate network functions into instructions and encapsulate the instructions into 128-bit IPv6 addresses, enabling network programming.
Computer Programming
Print "Hello World"
Human intent
Perform programming, implemented by computer language
Program
Convert the computer language into a CPU instruction
CPU instruction
Execute the instruction by server hardware
Server
Network Programming
Forward a service along a low-latency path
Network intent
Convert the service requirement into a network model
SDN controller
Encode the corresponding path as SRv6 segments and insert the segments into packets
SRv6 segment
Forward the packets by network devices
Network device

## Slide 14: IPv6 Segment Routing Header (SRH)
RFC 8754 defines the IPv6 SRH added to IPv6 packets. The SRH format is as follows:
The value 43 indicates a routing extension header.
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type=4 |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List [0] (128-bit IPv6 address) |  |  |  | 
Segment List [1] (128-bit IPv6 address) |  |  |  | 
Segment List [2] (128-bit IPv6 address) |  |  |  | 
Optional TLV objects (variable) |  |  |  | 
IPv6 Payload |  |  |  | 
An SRH contains the following fields:
  Segment List: an ordered list of SRv6 SIDs.
  Segments Left (SL): number of remaining segments. The SL value is decremented and the destination IP address (DIP) is changed to an active SID to complete traffic forwarding segment by segment.
  Tag: tags a packet as part of a class or group of packets to implement group-based policies.
  SRH TLVs (e.g. NSH metadata, HMAC TLV, and Padding TLV): can be used as global parameters of SIDs.
The recommended value of Routing Type for a routing extension header is 4, indicating an SRH.
Active segment
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)
Notes: The biggest difference between SRv6 and SR-MPLS lies in the IPv6 SRH. SRv6 uses IPv6 extension headers to implement Segment Routing.
For details, see "2. Segment Routing Header" at https://datatracker.ietf.org/doc/rfc8754/.

## Slide 15: SRv6 Network Programmability from the Perspective of SRHs
Leveraging programmable SRHs, SRv6 offers more powerful network programming capabilities than SR-MPLS.
Generally, SRHs provide a three-dimensional programming space:
  First dimension: segment list. In SRv6, multiple segments are sequentially combined to represent a specific SRv6 path. This is similar to the application of an MPLS label stack.
  Second dimension: flexible combination of fields in the 128-bit SRv6 SID. Each MPLS label contains four fixed-length fields: 20-bit label field, 8-bit Time to Live (TTL) field, 3-bit Traffic Class (TC) field, and 1-bit S field. In contrast, each SRv6 SID has 128 bits that can be flexibly divided into fields with variable lengths. This further demonstrates the programmability of SRv6.
  Third dimension: flexible combination of optional TLVs following segment lists. During packet transmission on a network, irregular information can be encapsulated in the forwarding plane by flexibly combining TLVs in SRHs.
Notes: Reference: SRv6 Network Programming: Ushering in a New Era of IP Networks

## Slide 16
SRv6 Overview
SRv6 Network Programming
  SRv6 Network Programming Overview
  SRv6 Segments & SRv6 Nodes
  SRv6 Instruction Sets
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 17: Network Instructions: SRv6 Segments
SRv6 segments are expressed using IPv6 addresses and usually called SRv6 segment identifiers (SIDs).
As shown in the figure, an SRv6 SID usually consists of three fields: Locator, Function, and Arguments. They are expressed in the Locator:Function:Arguments format. Note that the total length (Locator+Function+Arguments) is less than or equal to 128 bits. If the total length is less than 128 bits, the reserved bits are padded with 0s.
If the Arguments field does not exist, the format is Locator:Function. The Locator field occupies the most significant bits of an IPv6 address, and the Function field occupies the remaining part of the IPv6 address.
Locator
Function
Arguments
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)
128 bits
128 bits
128 bits
SRv6 segment: IPv6 address format
A computer instruction typically consists of an opcode and an operand. The former determines the operation to be performed; the latter determines the data, memory address, or both to be used in the computation. Similarly, network instructions, which are called SRv6 segments, need to be defined for SRv6 network programming.
Notes: https://datatracker.ietf.org/doc/draft-ietf-spring-srv6-network-programming/

## Slide 18: SRv6 Segment: Locator
The Locator field identifies the location of a network node, and is used for other nodes to route and forward packets to this identified node so as to implement network instruction addressing.
A locator has two important characteristics: routable and aggregatable. After a locator is configured for a node, the system generates a locator route and propagates the route throughout the SR domain using an IGP, allowing other nodes to locate the node based on the received route information. In addition, all SRv6 SIDs advertised by the node are reachable through the route.
In the following example, a locator with the 64-bit prefix 2001:DB8:ABCD:: is configured for a Huawei device.
Locator
Function
Arguments
128 bits
IPv6 prefix
[Router] segment-routing ipv6
[Router-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64
Notes: The locator is routable and therefore usually unique in an SR domain. In some scenarios, such as an anycast protection scenario, multiple devices may be configured with the same locator.

## Slide 19: SRv6 Segment: Function & Arguments
The Function field specifies the forwarding behavior to be performed, and is similar to the opcode in a computer instruction. In SRv6 network programming, forwarding behaviors are expressed using different functions. For example, RFC defines End, End.X, End.DX4, and End.DX6 behaviors.
End.X is similar to an adjacency SID in SR-MPLS and is used to identify a link. A configuration example is as follows:
Locator
Function
Arguments
128 bits
Opcode
Optional
[Router-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64
[Router-segment-routing-ipv6] opcode ::1 end-x interface G3/0/0 next-hop 2001:DB8:200::1
The opcode corresponding to the function is ::1. In this example, the Arguments field is not carried, and the SRv6 SID is 2001:db8:abcd::1.
This function guides packet forwarding from the specified interface (G3/0/0) to the corresponding neighbor (2001:DB8:200::1).
Notes: In some scenarios, an SRv6 endpoint behavior may require additional actions. In this case, the Arguments field must be encapsulated. For example, in an EVPN VPLS scenario where CE multi-homing is deployed for BUM traffic forwarding, the Function field is set to End.DT2M, and the Arguments field is used to provide local ESI mapping to implement split horizon.
The Function and Arguments fields can both be defined by engineers, resulting in an SRv6 SID structure that improves network programmability. In most scenarios, the Arguments field is not configured.

## Slide 20: SRv6 SID Examples
An End SID is an endpoint SID that identifies a destination node. It is similar to a node SID in SR-MPLS. After an End SID is generated on a node, the node propagates the SID to all the other nodes in the SRv6 domain through an IGP. All nodes in the SRv6 domain know how to implement the instruction bound to the SID.
An End.X SID is a Layer 3 cross-connect endpoint SID that identifies a link. It is similar to an adjacency SID in SR-MPLS. After an End.X SID is generated on a node, the node propagates the SID to all the other nodes in the SRv6 domain through an IGP. Although the other nodes can all obtain the SID, only the node generating the SID knows how to implement the instruction bound to the SID.
An End.DT4 SID is a PE-specific endpoint SID that identifies an IPv4 VPN instance. The instruction bound to the End.DT4 SID is to decapsulate packets and search the routing table of the corresponding IPv4 VPN instance for packet forwarding. The End.DT4 SID is equivalent to an IPv4 VPN label and used in L3VPNv4 scenarios. An End.DT4 SID can be either manually configured or automatically allocated by BGP within the dynamic SID range of the specified locator.
PE1
P
PE2
Loopback1
10.1.5.5/32
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
End SID
2001:DB8:1000::111
End SID
2001:DB8:2000::222
End SID
2001:DB8:3000::333
End.X SID
2001:DB8:1000::12
End.X SID
2001:DB8:2000::21
End.X SID
2001:DB8:2000::23
End.X SID
2001:DB8:3000::32
vpna: End.DT4 SID
2001:DB8:1000::1:0:1E
vpna: End.DT4 SID
2001:DB8:3000::1:0:1E

## Slide 21: SRv6 SID Configuration Commands (1)
[Huawei] segment-routing ipv6
Enable SRv6 and enter the SRv6 view.
After running the segment-routing ipv6 command, you can configure an IPv6 SID in the SRv6 view so that an IPv6 local SID forwarding entry can be generated.
[Huawei-segment-routing-ipv6] locator locator-name [ ipv6-prefix ipv6-address prefix-length [ [ static static-length ] | [ args args-length ] ] * ]
Configure an SRv6 SID locator.
An SRv6 SID is a 128-bit IPv6 address expressed in the Locator:Function:Arguments format.
The Locator field corresponds to the ipv6-prefix ipv6-address parameter and its length is determined by the prefix-length parameter.
The Function field is also called opcode, which can be dynamically allocated using an IGP or be configured using the opcode command. When configuring a locator, you can use the static static-length parameter to specify the static segment length, which determines the number of static opcodes that can be configured in the locator. In dynamic opcode allocation, the IGP allocates opcodes outside the range of the static segment, so that no SRv6 SID conflict occurs.
The Arguments field is determined by the args args-length parameter. This field is optional in SRv6 SIDs and depends on command configurations.
Notes: static static-length: specifies the static segment length in the Function field. This length determines the number of static opcodes that can be configured in the specified locator.
args args-length: specifies the length of the Arguments field. The Arguments field is located at the end of a SID. If args args-length is configured, the Arguments field is reserved and will not be occupied by configured static SIDs or generated dynamic SIDs.

## Slide 22: SRv6 SID Configuration Commands (2)
[Huawei-segment-routing-ipv6] opcode func-opcode end [ no-psp ]
3. Configure a static End SID opcode.
An End SID identifies an SRv6 node. The no-psp parameter is used to disable penultimate segment pop of the SRH (PSP).
[Huawei-segment-routing-ipv6] opcode func-opcode end-x interface { interface-name | interface-type interface-number } nexthop nexthop-address [ no-psp ]
4. Configure a static End.X SID opcode.
An End.X SID identifies a Layer 3 adjacency of an SRv6 node. Therefore, you need to specify an interface and the next hop address of the interface during the configuration.

## Slide 23: SRv6 SID Configuration Example
SRv6 SIDs can be statically configured or dynamically allocated. In dynamic allocation mode, only the locator command needs to be run, and the required opcode is dynamically allocated by an IGP. In static configuration mode, you need to run the opcode command to manually configure an opcode for the SIDs of the corresponding type.
The relationship of parameters in the locator command is as follows:
In static configuration mode, SIDs occupy only the static segment with values starting from 1, and the dynamic segment is set to 0. In dynamic allocation mode, SIDs occupy both the dynamic segment and static segment. The values in the dynamic segment start from 1, and those in the static segment start from 0.
In this example, the locator 2001:DB8:ABCD:: is configured, and its length is 64 bits. The static segment occupies 32 bits, the dynamic segment 32 bits, and the Args field 0 bits. The value range is as follows:
  Static segment: The start value is 2001:DB8:ABCD:0000:0000:0000:0000:0001, and the end value is 2001:DB8:ABCD:0000:0000:0000:FFFF:FFFF.
  Dynamic segment: The start value is 2001:DB8:ABCD:0000:0000:0001:0000:0000, and the end value is 2001:DB8:ABCD:0000:FFFF:FFFF:FFFF:FFFF.
|--Locator--|--Dynamic Opcode--|--Static Opcode--|--Args--|
[Router-segment-routing-ipv6] locator srv6_locator1 ipv6-prefix 2001:DB8:ABCD:: 64 static 32
Statically configuring End and End.X SIDs is recommended.
Dynamically allocated SIDs will change after a device restart, adversely affecting maintenance.

## Slide 24: SRv6 Nodes
RFC 8754 defines three types of SRv6 nodes:
  SRv6 source node: a source node that encapsulates packets with SRv6 headers.
  Transit node: an IPv6 node that forwards SRv6 packets but does not perform SRv6 processing.
  SRv6 segment endpoint node (endpoint node for short): destination node of SRv6 packets.
R1
FC01::1
Source Node
CE1
R2
Transit Node
FC02::2
R3
Endpoint Node
FC03::3
FC04::4
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node

## Slide 25: SRv6 Source Node
An SRv6 source node steers a packet using an SRv6 segment list. If the SRv6 segment list contains only one SID, and no Type Length Value (TLV) or other information needs to be added to the packet, the DA field of the packet is set to this SID.
An SRv6 source node can be either an SRv6-capable host where IPv6 packets originate or an edge device in an SRv6 domain.
The following figure shows an L3VPNv4 over SRv6 Policy scenario where IPv4 traffic is transmitted over SRv6. The SRv6 Policy's explicit path specifies that the traffic must pass through R3 and R4. The source node R1 is responsible for steering the IPv4 traffic into the corresponding tunnel and encapsulating an SRH.
IPv6 Header |  | 
SRH (SL = 2) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 
SRv6 Policy
R1
FC01::1
Source Node
CE1
R2
Transit Node
FC02::2
R3
Endpoint Node
FC03::3
FC04::4
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
Notes: Examples for the SRv6 source node to encapsulate an SRH:
  H.Insert: inserts an SRH into a received IP packet and searches the routing table for packet forwarding.
  H.Encaps: encapsulates an outer IPv6 header and SRH for a received IP packet, and searches the routing table for packet forwarding.
  H.Encaps.L2: encapsulates an outer IPv6 header and SRH for a received Layer 2 packet, and searches the routing table for packet forwarding.

## Slide 26: Transit Node
A transit node is an IPv6 node that does not participate in SRv6 processing on the SRv6 packet forwarding path. That is, the transit node just performs ordinary IPv6 packet forwarding.
After receiving an SRv6 packet, the node parses the IPv6 DA field in the packet. If the IPv6 DA is neither a locally configured SRv6 SID nor a local interface address, the node considers the SRv6 packet as an ordinary IPv6 packet and searches the routing table for packet forwarding without processing the SRH.
A transit node can be either an ordinary IPv6 node or an SRv6-capable node.
R1
FC01::1
Source Node
CE1
R2
Transit Node
FC02::2
R3
Endpoint Node
FC03::3
FC04::4
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
IPv6 Header |  | 
SRH (SL = 2) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 

## Slide 27: Endpoint Node
An endpoint node is a node that receives an SRv6 packet destined for itself (a packet of which the IPv6 destination address is a local SID).
For example, R4 searches its My Local SID table based on the IPv6 DA FC04::4 of the packet and finds a matching End SID. Then, R4 decrements the SL field by 1 and updates the IPv6 DA to the VPN SID FF04::400. Based on the VPN SID, R4 searches its My Local SID table, finds a matching End.DT4 SID, removes the SRH and IPv6 header, and forwards the packet to CE2.
R1
FC01::1
Source Node
CE1
R2
Transit Node
FC02::2
R3
Endpoint Node
FC03::3
FC04::4
R4
CE2
CE2: End.DT4
FC04::400
Endpoint Node
IPv6 Header |  | 
SRH (SL = 1) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 
IPv6 Header |  | 
SRH (SL = 0) |  | 
FC04::400 | FC04::4 | FC03::3
Payload |  | 

## Slide 28: SRv6 Packet Forwarding Summary: SRH Processing
In SRv6 forwarding, each time a packet passes through an SRv6 node, the SL field is decremented by 1 and the IPv6 DA changes. An IPv6 DA is determined by both the SL and Segment List fields.
SRH (SL = n)
(Segment List [0],
Segment List [1],
…,
Segment List [n – 1],
Segment List [n])
IPv6 DA=
Segment List [n]
SRH (SL = n – 1)
(Segment List [0],
Segment List [1],
…,
Segment List [n – 1],
Segment List [n])
IPv6 DA=
Segment List [n – 1]
SRv6 Source Node
Segment List [n]
Segment List [n – 1]
Segment List [1]
Segment List [0]
SRH (SL = 1)
(Segment List [0],
Segment List [1],
…,
Segment List [n – 1],
Segment List [n])
IPv6 DA=
Segment List [1]
SRH (SL = 0)
(Segment List [0],
Segment List [1],
…,
Segment List [n – 1],
Segment List [n])
IPv6 DA=
Segment List [0]
Different from SR-MPLS label processing, SRv6 SRH processing is implemented from the bottom up, and segments in the SRv6 SRH are not popped after being processed by a node. Therefore, the SRv6 header retains path information, which can be used for path backtracking.

## Slide 29
SRv6 Overview
SRv6 Network Programming
  SRv6 Network Programming Overview
  SRv6 Segments & SRv6 Nodes
  SRv6 Instruction Sets
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 30: SRv6 Instruction Sets
The SRH stores an ordered list of instructions for implementing network services, and it is equivalent to a computer program. Segment List [0] to Segment List [n] are equivalent to the instructions of the computer program. The first instruction to be executed is Segment List [n]. The SL field, which is equivalent to the program counter (PC) of the computer program, points to the instruction that is being executed
ietf-spring-srv6-network-programming defines many behaviors, which are also called instructions.
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next=43 | Hop Limit
Source Address |  |  |  | 
Destination Address |  |  |  | 
Next Header | Hdr Ext Len | Routing Type=4 |  | Segments Left
Last Entry | Flags | Tag |  | 
Segment List [0] (128-bit IPv6 address) |  |  |  | 
Segment List [1] (128-bit IPv6 address) |  |  |  | 
Segment List [2] (128-bit IPv6 address) |  |  |  | 
Optional TLV objects (variable) |  |  |  | 
IPv6 Payload |  |  |  | 
IPv6 Payload
IPv6 Header
IPv6 SRH (IPv6 Extension Header)

## Slide 31: SRv6 Instruction Sets: Endpoint Node Behaviors
Behaviors defined by SRv6 instruction sets are classified as endpoint node behaviors and source node behaviors.
Common endpoint node behaviors are as follows.
Instruction | Function Description | Application Scenario
End | Copies the next SID to the IPv6 DA and searches the forwarding table for packet forwarding. | Used for packet forwarding through a specified node. An End SID is similar to an SR-MPLS node segment.
End.X | Forwards a packet through a specified outbound interface. | Used for packet forwarding through a specified outbound interface. An End.X SID is similar to an SR-MPLS adjacency segment.
End.T | Searches a specified IPv6 routing table for packet forwarding. | Used in scenarios where multiple routing tables exist.
End.DX2 | Decapsulates a packet and forwards it through a specified Layer 2 outbound interface. | Used in L2VPN scenarios, such as EVPN virtual private wire service (VPWS).
End.DX4 | Decapsulates a packet and forwards it over a specified IPv4 Layer 3 adjacency. | Used in L3VPNv4 scenarios where packets are forwarded to a CE through a specified IPv4 adjacency.
End.DX6 | Decapsulates a packet and forwards it over a specified IPv6 Layer 3 adjacency. | Used in L3VPNv6 scenarios where packets are forwarded to a CE through a specified IPv6 adjacency.
End.DT6 | Decapsulates a packet and searches a specified IPv6 routing table for packet forwarding. | Used in L3VPNv6 scenarios.
End.DT4 | Decapsulates a packet and searches a specified IPv4 routing table for packet forwarding. | Used in L3VPNv4 scenarios.
End.B6.Insert | Inserts an SRH and applies a specified SRv6 Policy. | Used in scenarios such as traffic steering into an SRv6 Policy in Insert mode, tunnel stitching, and software-defined networking in a wide area network (SD-WAN) route selection.
End.BM | Inserts an MPLS label stack and applies a specified SR-MPLS Policy. | Used in SRv6 and SR-MPLS interworking scenarios.
Notes: For more endpoint behaviors, see ietf-spring-srv6-network-programming.

## Slide 32: Naming Rules for SRv6 Instructions
SRv6 instructions are named according to certain rules. You can quickly determine the instruction function based on the naming rule combination.
  End: the most basic instruction executed by a segment endpoint node, directing the node to terminate the current instruction and start the next instruction. The corresponding forwarding behavior is to decrement the SL field by 1 and copy the SID pointed by the SL field to the DA field in the IPv6 header.
  X: forwards packets through one or a group of Layer 3 outbound interfaces.
  T: searches a specified routing table and forwards packets.
  D: decapsulates packets by removing the IPv6 header and related extension headers.
  V: searches a specified table for packet forwarding based on virtual local area network (VLAN) information.
  U: searches a specified table for packet forwarding based on unicast MAC address information.
  M: searches a Layer 2 forwarding table for multicast forwarding.
  B6: applies a specified SRv6 Policy.
  BM: applies a specified SR-MPLS Policy.

## Slide 33: SRv6 Instruction Sets: Source Node Behaviors
An SRv6 source node steers packets into an SRv6 Policy and, if possible, encapsulates SRHs into the packets. The following table lists the behaviors of an SRv6 source node.
Source Node Behavior | Function Description
H.Insert | Inserts an SRH into a received IPv6 packet and searches the corresponding routing table for packet forwarding.
H.Insert.Red | Inserts a reduced SRH into a received IPv6 packet and searches the corresponding routing table for packet forwarding.
H.Encaps | Encapsulates an outer IPv6 header and SRH for a received IP packet, and searches the corresponding routing table for packet forwarding.
H.Encaps.Red | Encapsulates an outer IPv6 header and reduced SRH for a received IP packet, and searches the corresponding routing table for packet forwarding.
H.Encaps.L2 | Encapsulates an outer IPv6 header and SRH for a received Layer 2 frame, and searches the corresponding routing table for forwarding.
H.Encaps.L2.Red | Encapsulates an outer IPv6 header and reduced SRH for a received Layer 2 frame, and searches the corresponding routing table for forwarding.

## Slide 34: SRv6 Instruction Sets: Flavors
Flavors are additional behaviors defined to enhance End series instructions. These behaviors are optional and used to meet diverse service requirements.
SRv6-Network-Programming defines the following additional behaviors: PSP, Ultimate Segment Pop of the SRH (USP), and Ultimate Segment Decapsulation (USD).
Flavor | Function Description | Attached End Instruction
PSP | Removes the SRH on the penultimate endpoint node. | End, End.X, and End.T
USP | Removes the SRH on the ultimate endpoint node. | End, End.X, and End.T
USD | Decapsulates the outer IPv6 header on the ultimate endpoint node. | End, End.X, and End.T
Notes: Different flavors can be combined. For example, if an End SID carries PSP and USP flavors, the PSP action is performed on the penultimate node, and the USD action is performed on the ultimate node.

## Slide 35
SRv6 Overview
SRv6 Network Programming
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 36: SRv6 Policy Overview
SR-TE Policy is an application of SR Policy in the traffic engineering field. It leverages the source routing mechanism of SR to guide packet forwarding based on an ordered list of segments encapsulated by the headend. SR-TE Policy does not involve traditional tunnel interfaces.
SR-TE Policy is classified as SR-MPLS Policy or SRv6 Policy by segment. This document uses SRv6 Policy as an example.
SR Policy is the SR-TE implementation mode of mainstream vendors. In the following contents, SRv6 Policy will be used to refer to SRv6 TE Policy.
<PE1>display tunnel-info all
Tunnel ID Type Destination Status
----------------------------------------------------------------------------------------
0x0000000001004c4c04 ldp 1.0.0.12 UP
0x000000002900000004 srbe-lsp 1.0.0.12 UP
0x000000000300002001 sr-te 1.0.0.12 UP
0x00000000320000c001 srtepolicy 1.0.0.12 UP
0x000000003400002001 srv6tepolicy FC01::12 UP
Notes: https://datatracker.ietf.org/doc/draft-ietf-spring-segment-routing-policy/
An SR Policy is a framework that enables instantiation of an ordered list of segments on a node for implementing a source routing policy with a specific intent for traffic steering from that node.

## Slide 37: SR Policy Standards
BGP-LS/BGP IPv6 SR Policy
Controller
According to RFC draft-ietf-spring-segment-routing-policy, BGP multi-protocol extension supports the BGP IPv6 SR Policy (SAFI = 73) address family for SR Policy delivery.
The controller uses BGP to deliver a combination of SR SIDs to the ingress. A TE tunnel carrying the policy color and destined for the egress is then created on the ingress.
If the tunnel needs to be referenced, it can be located based on the policy color.
Color
Ingress
Egress
Notes: There are three mainstream methods for SR Policy implementation.
  BGP: BGP-LS is used to collect topology information, so that no new interface protocol needs to be introduced for customer-developed controllers. BGP IPv6 SR Policy is used to deliver route information.
  PCEP: PCEP is a mature southbound protocol used in SR-MPLS TE scenarios. However, the tunnel implementation models of vendors are different and cannot interwork, and the interaction process of PCEP is more complex than that of BGP. As such, BGP extension is recommended.
  NETCONF/YANG: delivers tunnel paths to forwarders as configurations. This method is not recommended because it delivers configurations in essence and offers the poorest performance. In a comprehensive solution, NETCONF is used to deliver configurations other than tunnel configurations.
For details about SR Policy, see [I-D.ietf-spring-segment-routing-policy]. (https://datatracker.ietf.org/doc/draft-ietf-idr-segment-routing-te-policy/)

## Slide 38: SR Policy Solution Architecture
Huawei SR Policy solution architecture involves three key protocols: BGP-LS, BGP IPv6 SR Policy, and NETCONF.
  BGP-LS collects tunnel topology information used to compute SR Policy paths and display tunnel status.
  BGP IPv6 SR Policy is used by the controller to deliver SR Policy information (e.g. color, headend, and endpoint).
  NETCONF is used to deliver other configurations, such as service interfaces and route-policies (with the color attribute).
1. BGP-LS
Controller
Color
Ingress
Egress
2. BGP IPv6 SR Policy
3. NETCONF
Notes: BGP-LS connection:
  Collects tunnel topology information for SR Policy path computation.
  BGP-LS supports the collection of SR Policy status information, based on which the controller displays tunnel status. https://datatracker.ietf.org/doc/draft-ietf-idr-te-lsp-distribution/
  BGP-LS supports Segment Routing Local Block (SRLB) information encapsulation and decapsulation, so that the controller can obtain the SRLB information for binding SID allocation. (The backup path of each SR Policy corresponds to a binding SID.).
BGP IPv6 SR Policy connection:
  The controller delivers SR Policy information to forwarders to generate SR Policies.
  BGP routes delivered by the controller carry the color community attribute, and this attribute can be transmitted. The ingress finds a matching BGP route and recurses it to an SR Policy based on the color and endpoint information.
  In the SR Policy solution, path computation constraints of each application need to be planned in a unified manner on the controller based on SLAs, different colors are used to identify SR Policies. An SR Policy is uniquely identified by <headend, color, endpoint>. The BGP route of services to be steered into an SR Policy needs to carry the corresponding color attribute.

## Slide 39: SRv6 Policy Tuple
An SRv6 Policy is identified by <headend, color, endpoint>. For a specified node, the policy is identified by <color, endpoint>.
  Headend: node where an SRv6 Policy is originated. Generally, it is a globally unique IP address.
  Color: 32-bit extended community attribute. It is used to identify a type of service intent (e.g. low latency).
  Endpoint: destination address of an SRv6 Policy. Generally, it is a globally unique IP address.
Color and endpoint are used to identify a forwarding path on the specific headend of an SRv6 Policy.

## Slide 40: SRv6 Policy Model
One SRv6 Policy may contain multiple candidate paths with the preference attribute. The valid candidate path with the highest preference functions as the primary path of the SRv6 Policy, and the valid candidate path with the second highest preference functions as a backup path.
A candidate path is an SRv6 Policy's segment list sent to the headend through PCEP or BGP IPv6 SR Policy.
Weights can be configured for segment lists to control load balancing among SR paths.
SRv6 Policy
Candidate path 1
Preference 200
Candidate path 2
Preference 100
Segment list 1
Weight
Segment list 2
Weight
Segment list 1
Weight
Primary path
Backup path
SR policy P1 <headend, color, endpoint>
Candidate-path CP1 <protocol, origin, discriminator>
Preference 200
Weight W1, SID-List1 <SID11...SID1i>
Weight W2, SID-List2 <SID21...SID2j>
Candidate-path CP2 <protocol, origin, discriminator>
Preference 100
Weight W3, SID-List3 <SID31...SID3i>
Weight W4, SID-List4 <SID41...SID4j>
<headend, color, endpoint>
Notes: SR Policy P1 is uniquely determined by the triplet <headend, color, endpoint>.
An SR Policy can contain multiple candidate paths (e.g. CP1 and CP2). Each of the paths is uniquely determined by the triplet <protocol, origin, discriminator>.
CP1 is the primary path because it is valid and has the highest preference. The two SID lists of CP1 are delivered to the forwarder, and traffic is balanced between the two paths based on weights. For SID-List <SID11...SID1i>, traffic is balanced according to W1/(W1+W2).

## Slide 41: Extension: BGP IPv6 SR Policy Routing Table
An SR Policy is represented as [distinguisher][policycolor][endpoint] in the BGP routing table.
<PE1>display bgp sr-policy ipv6 routing-table
BGP Local router ID is 1.0.0.1
Status codes: * - valid, > - best, d - damped, x - best external, a - add path,
h - history, i - internal, s - suppressed, S - Stale
Origin : i - IGP, e - EGP, ? - incomplete
RPKI validation codes: V - valid, I - invalid, N - not-found
Total Number of Routes: 2
Network Nexthop MED LocPrf PrefVal Path/Ogn
*>i [10][5][FC01::12] 2000::102 4294967286 100 0 ?
*>i [14][3][FC01::12] 2000::102 4294967286 100 0 ?

## Slide 42: Extension: BGP IPv6 SR Policy's Tunnel Encapsulation Attribute (1)
In a BGP Update message, path attributes carry specific candidate path information. The following shows the Tunnel Encapsulation Attribute format.
SR Policy SAFI NLRI: <Distinguisher, Policy-Color, Endpoint>
Attributes:
Tunnel Encaps Attribute (23)
Tunnel Type: SR Policy (15)
Binding SID
Preference
Priority
Policy Name
Explicit NULL Label Policy (ENLP)
Segment List
Weight
Segment
Segment
…
Notes: RFC-Advertising Segment Routing Policies in BGP
The BGP extensions for the advertisement of SR Policies include the following components:
  New SAFI
  New Tunnel Type ID and a series of TLVs to be inserted into the Tunnel Encapsulation Attribute
  Route-target extended community used to indicate the intended headend of SR Policy advertisement
  Color extended community for traffic steering (defined in [I-D.ietf-idr-tunnel-encaps])

## Slide 43: Extension: BGP IPv6 SR Policy‘s Tunnel Encapsulation Attribute (2)
The BGP IPv6 SR Policy routing table contains complete tunnel encapsulation attribute information.
<PE1>display bgp sr-policy ipv6 routing-table [10][5][FC01::12]
BGP local router ID : 1.0.0.1
Local AS number : 100
Paths: 1 available, 1 best, 1 select, 0 best-external, 0 add-path
BGP routing table entry information of [10][5][FC01::12]:
From: 2000::102 (172.21.17.102)
Route Duration: 3d22h20m53s
Relay IP Nexthop: ::
Relay IP Out-Interface:GigabitEthernet0/0/0
Original nexthop: 2000::102
Qos information : 0x0
Ext-Community: RT <1.0.0.1 : 0>, SoO <172.21.17.102 : 0>
AS-path Nil, origin incomplete, MED 4294967286, localpref 100, pref-val 0, valid, internal, best, select, pre 255
…
Tunnel Encaps Attribute (23):
Tunnel Type: SR Policy (15)
Preference: 200
Binding SID: FC00:1::1:1, s-flag(0), i-flag(0)
Segment List
Weight: 1
Path MTU: 9600
Segment: type:2, SID: FC00:1::1:3D
Segment: type:2, SID: FC00:2::1:22
Segment: type:2, SID: FC00:6::1:24
Segment: type:2, SID: FC00:4::1:26
Segment List
Weight: 1
Path MTU: 9600
Segment: type:2, SID: FC00:11::1:20
Segment: type:2, SID: FC00:4::1:20
Segment: type:2, SID: FC00:3::1:24
Template ID: 4294967279
Not advertised to any peer yet

## Slide 44
SRv6 Overview
SRv6 Network Programming
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations

## Slide 45: Fast Service Provisioning
Provisioning Time
Months
Days
Cross-department Collaboration
5+
1
Number of Service Configuration Points
6+
2
Services are configured only on edge nodes, simplifying network management.
SRv6 underlay network
EVPN
EVPN
An ISP deploys SRv6 over native IPv6 to seize market opportunities.
Notes: A traditional network adopts the segmented networking and separate management mode. The bearer technologies used on the segmented network are not integrated, and different network segments need to be managed and maintained by different departments. As such, cross-domain service provisioning usually requires multiple departments (5+) to collaborate, slowing down the provisioning. SRv6 implements E2E collaboration on a cross-domain network. Cross-domain seamless connections can be automatically set up on the service network only by enabling SRv6 at the two ends of the network. Transit nodes are unaware of new services and do not require any changes. Through cross-domain E2E collaboration, the service network deployment time is reduced from months to days.

## Slide 46: SRv6 VPN Overlay Native IPv6
The Function field is programmed to identify the VPN: B8::D100. No SRH is encapsulated, and VPN services are implemented using native IPv6.
Locator for addressing to R8
Function that identifies a VPN
VRF 100
R1
R2
R3
R4
R5
R6
R7
R8
The ingress encapsulates data.
Transit nodes perform only IPv6 forwarding.
The egress decapsulates the data.
Locator: B8::/96
End.DT4: B8::D100
User Data
SA=R5 DA=B8::D100
User Data
User Data
SA=R5 DA=B8::D100
User Data
Notes: SRv6 provides overlay VPN capabilities on native IPv6 networks to isolate different services.
For a VPN service, a PE of the VPN service generates a VPN SID for the corresponding VPN instance, with the Locator field indicating the reachability information about the local node and the Function field identifying the VPN. As shown in the figure, R8 allocates VPN SID B8::D100 to VPN 100. B8 indicates the locator used to identify how the service can reach R8. D100 identifies the VPN and is used for service addressing and forwarding in VRF 100. The VPN SID is advertised together with VPN routes to all other PEs through BGP extension, and a local SID forwarding entry is delivered.
When VPN service data reaches the ingress, the ingress searches for the corresponding VPN SID based on the VPN route and performs SRv6 encapsulation. After R5 receives the VPN packet destined for R8, R5 searches the local VPN forwarding table, finds the forwarding entry corresponding to VPN 100, and performs IPv6 encapsulation using the VPN SID B8::D100 allocated by R8 as the destination address. After packet encapsulation is completed, the ingress searches for the outbound interface and next hop based on the destination IPv6 address and forwards the packet accordingly.
The packet finally reaches R8. R8 then searches the local SID forwarding table based on the destination address, finds the routing entry corresponding to the VPN, and forwards the VPN packet. This is the complete VPN packet forwarding process.
SRv6-based VPN packet forwarding does not require additional encapsulation protocols. SRv6 tunnels natively support multi-point interworking, and therefore you do not need to manually configure tunnels one by one. IPv6 services need to be deployed only on edge nodes that are aware of services, and transit nodes only need to perform native IPv6 forwarding. This simplifies VPN network deployment and maintenance. In addition, the IPv6 route aggregation capability enables edge nodes to maintain only aggregated or default routes, reducing the burden on edge nodes on a large-scale network.

## Slide 47: Flexible Path Control
R1
R2
R3
R4
R5
R6
R7
R8
Network congestion, packet loss, and large latency
Network congestion or fault
Controller
Information collection
Path orchestration
Programmable service path (R2->R7->R8)
R8
R7
R2
SA=R5 DA=R2
User Data
User Data
Computes congestion-free and low-latency paths based on collected information.
User Data
Flexible path control improves user experience in data services.
Notes: SRv6 implements service path programming through flexible segment list orchestration, thereby achieving service-driven network path selection. With the help of an SDN controller, SRv6 ensures that services are always transmitted over network paths meeting service requirements.
The SDN controller collects network information in real time to obtain and maintain current network status and relevant information. To meet customers' SLA requirements, such as low latency, bandwidth guarantee, and primary and secondary paths, the controller computes and orchestrates the optimal network path based on the current network status. In addition, the controller delivers the orchestrated service path to the ingress to guide service forwarding on the network. For example, the service path R2->R7->R8 is delivered, as shown in the figure. After the user service packet reaches R5, SRv6 encapsulation is performed for it, and the destination address is set to the next SID, that is, R2 (the first SID to be encapsulated in the path).
During service running, IFIT can be used to measure service quality in real time, and Telemetry can be used to collect measurement data in real time. Based on technologies such as big data analytics and machine learning, the SDN controller analyzes service quality on the network in real time. When service quality deteriorates, the SDN controller can re-trigger service path computation and switch service flows to a new path that meets SLA requirements.
Through flexible service path control as well as network status awareness and collection, SRv6 implements real-time service quality measurement and assurance, ensuring user experience.

## Slide 48: Large-Scale Network Slicing
SRv6 SID 1
SRv6 SID 2
SRv6 SID 3
Default slice
Service slice 1
Service slice 2
Slice ID 1
Slice ID 2
Default slice
Service slice 1
Service slice 2
Slice ID 1
Slice ID 2
Physical interface on R1
Physical interface on R2
Physical interface on R3
On an SRv6 network, service packets carry slice information.
The SRv6+Flex-E solution provides private network guarantee for high-value services.
SRv6 SIDs identify main interface information.
Slice IDs identify service slices and are transmitted hop by hop.
Control and Forwarding Decoupling
1000+ Slices Function Like Private Networks
A single routing protocol centrally manages 1000+ slices.
Services are isolated between slices, providing private network-like service experience.
Notes: In a traditional slicing solution, different IP addresses need to be configured for network slices and an IGP needs to be run for route distribution. This implementation mode requires a lot of configurations. In addition, because different slices must have independent IP addresses, the IGP route quantity increases exponentially with the number of slices. This increases the burden on network devices and limits the large-scale deployment of slices.
In the SRv6+Slice ID solution, SRv6 SIDs identify network nodes, and slice IDs identify slices. All slices share the SID and IP address of the default slice, and slice IDs are used to differentiate slices. The SRv6 network programmability enables the data plane to be separated from the control plane, preventing the IGP load from affecting the slicing scale and allowing 1000+ slices to be created to meet the increasingly diversified slicing requirements in the future.

## Slide 49: APN, Enabling Application-Driven Network Programming
Access and cloud PEs construct high-quality channels based on application information.
Carrier network
Carrier's bearer network
Cloud bearer network
Application ID identification
Enterprise intranet
Access PE
Cloud PE
Access and cloud PEs implement network programming based on application IDs.
Application ID identification
Application-driven network programming: application ID information transmission hop by hop
Cloud
HUAWEI CLOUD uses APN to ensure WeLink service experience, helping enterprises implement borderless collaboration.
IPv6 extension header
IPv6 extension header
Notes: SRv6 programmability enables networks to interact with applications, implementing application-based refined network traffic operation and management. For example, HUAWEI CLOUD can ensure WeLink service experience based on SRv6 APN. As shown in the figure, the network devices at the enterprise egress and cloud egress identify applications and transmit application information to the access and cloud PEs through IPv6 extension headers. According to specified service policies, the PEs perform differentiated service path orchestration based on application IDs so as to implement application-based differentiated service operation.

## Slide 50
SRv6 Overview
SRv6 Network Programming
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations
  SRv6 BE
  SRv6 Policy

## Slide 51: L3VPNv4 over SRv6 BE (1)
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SRv6 BE paths on the backbone network to enable CE1 and CE2 to communicate through Loopback1.
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Notes: The experiment configuration is based on the NE20E-S2F (software version: NE20E V800R012C10SPC300). The configuration roadmaps for different devices are similar. For details, see the corresponding product documentation.

## Slide 52: L3VPNv4 over SRv6 BE (2)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Establish an MP-IBGP peer relationship between the PEs.
[~PE1] bgp 100
[~PE1-bgp] peer 2001:DB8:3::3 as-number 100
[*PE1-bgp] peer 2001:DB8:3::3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
Check the VPNv4 peer relationship on PE1.
<PE1>display bgp vpnv4 all peer
BGP local router ID : 10.0.1.1
Local AS number : 100
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent Up/Down State
2001:DB8:3::3 4 100 3 4 00:00:04 Established

## Slide 53: L3VPNv4 over SRv6 BE (3)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
Establish an SRv6 BE path between the PEs. The configuration on PE1 is as follows: (The configuration on PE2 is not provided here, and the P does not require such configuration.)
[~PE1] segment-routing ipv6
[*PE1-segment-routing-ipv6] encapsulation source-address 2001:DB8:1::1
[*PE1-segment-routing-ipv6] locator as100 ipv6-prefix 2001:DB8:100:: 64 static 32
[*PE1-segment-routing-ipv6-locator] quit
[*PE1-segment-routing-ipv6] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 prefix-sid
[*PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
[~PE1] isis 1
[~PE1-isis-1] segment-routing ipv6 locator as100
[*PE1-isis-1] commit
[~PE1-isis-1] quit
Notes: Configure basic SRv6 functions as follows:
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the encapsulation source-address ipv6-address [ ip-ttl ttl-value ] command to configure a source address for SRv6 VPN encapsulation.
    When traffic enters an SRv6 VPN tunnel, the address configured using this command functions as the source address in the IPv6 header. The source address must be an existing interface address on the device.
  Run the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command to configure an SRv6 locator.
    The Locator field corresponds to the ipv6-prefix ipv6-address parameter and its length is determined by the prefix-length parameter. A locator identifies an IPv6 subnet on which all IPv6 addresses can be allocated as SRv6 SIDs. After a locator is configured for a node, the system generates a locator route through which other nodes can locate this node. In addition, all SIDs advertised by the node are reachable through the route.
    The Function field is also called opcode, which can be dynamically allocated using an IGP or be configured using the opcode command. When configuring a locator, you can use the static static-length parameter to specify the static segment length, which determines the number of static opcodes that can be configured in the locator. In dynamic opcode allocation, the IGP allocates opcodes outside the range of the static segment, so that no SRv6 SID conflict occurs.

## Slide 54
Notes:   (Optional) Run the opcode func-opcode end-dt4 vpn-instance vpn-instance-name command to configure a static SID opcode.
    An End.DT4 SID can be either dynamically allocated through BGP or manually configured. If you want to use the segment-routing ipv6 locator locator-name command to enable dynamic End.DT4 SID allocation by BGP in the future, skip this step.
  Run the quit command to exit the SRv6 locator view.
  Run the quit command to exit the SRv6 view.
Enable IS-IS SRv6.
  Run the isis [ process-id ] command to enter the IS-IS view.
  Run the ipv6 enable topology ipv6 command to enable the IPv6 capability for the IS-IS process in the IPv6 topology.
  Run the segment-routing ipv6 locator locator-name [ auto-sid-disable ] command to enable IS-IS SRv6.
    segment-routing ipv6 locator locator-name: enables IS-IS SRv6 and dynamic SID allocation. SIDs must be allocated within the locator range.
    segment-routing ipv6 locator locator-name auto-sid-disable: enables IS-IS SRv6 and disables dynamic SID allocation so that SIDs are statically allocated within the locator range.
    During SRv6 SID allocation, if a static opcode is configured, the static opcode is preferentially used to form a static SID. If no static opcode is configured, a SID is dynamically allocated. The process of dynamic SRv6 SID allocation using IS-IS is as follows:
    Configure a locator in the SRv6 view, and run the segment-routing ipv6 locator command in the IS-IS process view to enable SRv6 and reference the locator. An IS-IS process can reference multiple locators. However, only one locator can be used to advertise End/End.X SIDs.
    IS-IS allocates an End SID to each locator in the range of the dynamic segment based on locator configurations. Both PSP and non-PSP SIDs can be allocated.
    Configure IPv6 addresses for interfaces and enable IS-IS IPv6. IS-IS allocates both PSP and non-PSP End.X SIDs to the interfaces in the range of the dynamic segment based on locator configurations.
  Run the quit command to exit the IS-IS view.
Configure the device to add SIDs to VPN routes.
  Run the peer ipv6-address prefix-sid command to enable the device to exchange IPv4 prefix SID information with the specified IPv6 peer.

## Slide 55: L3VPNv4 over SRv6 BE (4)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
Enable the VPN instance IPv4 address family on each PE. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[~PE1] bgp 100
[*PE1-bgp] ipv4-family vpn-instance vpna
[*PE1-bgp-vpna] peer 10.0.14.4 as-number 65000
[*PE1-bgp-vpna] segment-routing ipv6 best-effort
[*PE1-bgp-vpna] segment-routing ipv6 locator as100
[*PE1-bgp-vpna] commit
[~PE1-bgp-vpna] quit
[~PE1-bgp] quit
Notes: Configure VPN routes to recurse to SRv6 BE paths based on the carried SIDs.
  Run the bgp {as-number-plain | as-number-dot} command to enter the BGP view.
  Run the ipv4-family vpn-instance vpn-instance-name command to enter the BGP-VPN instance IPv4 address family view.
  Run the segment-routing ipv6 best-effort command to enable VPN route recursion based on the SIDs carried by routes.
  Run the segment-routing ipv6 locator locator-name [ auto-sid-disable ] command to enable the device to add SIDs to VPN routes.
  If auto-sid-disable is not specified, dynamic SID allocation is supported. If there are static SIDs in the range of the locator specified using locator-name, the static SIDs are used. Otherwise, dynamically allocated SIDs are used. If auto-sid-disable is specified, BGP does not dynamically allocate SIDs.
  Run the commit command to commit the configuration.

## Slide 56: L3VPNv4 over SRv6 BE (5)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Check the local SID table containing all types of SRv6 SIDs on PE2.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
<PE2>display segment-routing ipv6 local-sid forwarding
My Local-SID Forwarding Table
-------------------------------------
SID : 2001:DB8:300::1:0:0/128 FuncType : End
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:1/128 FuncType : End
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:2/128 FuncType : End.X
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:3/128 FuncType : End.X
LocatorName: as100 LocatorID: 2
SID : 2001:DB8:300::1:0:20/128 FuncType : End.DT4
LocatorName: as100
PE2 locally generates an End.DT4 SID and advertises the SID to PE1.

## Slide 57: L3VPNv4 over SRv6 BE (6)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Check VPNv4 routing information on PE1.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
<PE1>display bgp vpnv4 al routing-table 10.1.5.5
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 10.1.5.5/32:
Label information (Received/Applied): 3/NULL
From: 2001:DB8:3::3 (10.0.3.3)
Route Duration: 0d00h15m54s
Relay IP Nexthop: FE80::DE99:14FF:FE7A:C301
Relay IP Out-Interface: GigabitEthernet0/3/0.12
Relay Tunnel Out-Interface:
Original nexthop: 2001:DB8:3::3
Qos information : 0x0
Ext-Community: RT <111 : 1>
Prefix-sid: 2001:DB8:300::1:0:20
AS-path Nil, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 20
Not advertised to any peer yet
IPv6 address of the peer;
SID corresponding to 10.1.5.5 (the same as that locally allocated on PE2)

## Slide 58: L3VPNv4 over SRv6 BE (7)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
<PE1> display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Route Flags: R - relay, D - download to fib, T - to vpn-instance, B - black hole route
------------------------------------------------------------------------------
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 2001:DB8:300::1:0:20 Neighbour: 2001:DB8:3::3
State: Active Adv Relied Age: 00h17m40s
Tag: 0 Priority: low
Label: 3 QoSInfo: 0x0
IndirectID: 0x1000177 Instance:
RelayNextHop: 2001:DB8:300::1:0:20 Interface: SRv6 BE
TunnelID: 0x0 Flags: RD
Check vpna's routing information on PE1.
PE1 uses this IPv6 address as the next-hop address to forward packets destined for 10.1.5.5.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.
Interface type: SRv6 BE

## Slide 59: L3VPNv4 over SRv6 BE (8)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 BE path on the backbone network.
Enable the VPN instance IPv4 address family on each PE.
Establish an MP-IBGP peer relationship between the PEs.
Verify the configuration.

## Slide 60
SRv6 Overview
SRv6 Network Programming
SRv6 Policy Overview
Typical SRv6 Applications
Basic SRv6 Configurations
  SRv6 BE
  SRv6 Policy

## Slide 61: L3VPNv4 over SRv6 Policy (1)
PE1
P
PE2
2001:DB88:12::/96
Loopback0
2001:DB8:1::1/128
Loopback1
10.1.5.5/32
Networking requirements:
Connect PE1 and PE2 to different CEs that belong to VPN instance vpna.
Deploy L3VPN service recursion to SRv6 Policies on the backbone network to enable CE1 and CE2 to communicate through Loopback1.
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
Loopback0
2001:DB8:2::2/128
Loopback0
2001:DB8:3::3/128
2001:DB88:23::/96
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.

## Slide 62: L3VPNv4 over SRv6 Policy (2)
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Establish an MP-IBGP peer relationship between the PEs.
[~PE1] bgp 100
[~PE1-bgp] peer 2001:DB8:3::3 as-number 100
[*PE1-bgp] peer 2001:DB8:3::3 connect-interface loopback 0
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 enable
[*PE1-bgp-af-vpnv4] commit
[~PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
Check the VPNv4 peer relationship on PE1.
<PE1>display bgp vpnv4 all peer
BGP local router ID : 10.0.1.1
Local AS number : 100
Total number of peers : 1 Peers in established state : 1
Peer V AS MsgRcvd MsgSent Up/Down State
2001:DB8:3::3 4 100 3 4 00:00:04 Established
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
Notes: The SIDs of PE1, the P, and PE2 are 2001:DB8:1000::111, 2001:DB8:2000::222, and 2001:DB8:3000::333, respectively.
In this experiment, the SRv6 Policy is established based on specified End SIDs.

## Slide 63: L3VPNv4 over SRv6 Policy (3)
Configure an SRv6 SID. PE1 configurations are as follows: (P and PE2 configurations are not provided.)
[~PE1] segment-routing ipv6
[*PE1-segment-routing-ipv6] encapsulation source-address 2001:DB8:1::1
[*PE1-segment-routing-ipv6] locator as1000 ipv6-prefix 2001:DB8:1000:: 64 static 32
[*PE1-segment-routing-ipv6-locator] opcode ::111 end
[*PE1-segment-routing-ipv6-locator] quit
[*PE1-segment-routing-ipv6] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 prefix-sid
[*PE1-bgp-af-vpnv4] quit
[~PE1-bgp] quit
[~PE1] isis 1
[~PE1-isis-1] segment-routing ipv6 locator as1000 auto-sid-disable
[*PE1-isis-1] commit
[~PE1-isis-1] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Manually configure an SRv6 End SID.
Notes: SRv6 paths are established using SIDs. Static SRv6 SIDs are recommended. The configuration procedure is as follows:
  Run the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command to configure an SRv6 locator.
  Run the opcode func-opcode end command to configure a static End SID opcode.
  Run the opcode func-opcode end-x interface interface-name nexthop nexthop-address [ no-psp ] command to configure a static End.X SID opcode.
  Run the quit command to exit the SRv6 locator view.

## Slide 64: L3VPNv4 over SRv6 Policy (4)
Configure an SRv6 Policy. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] segment-routing ipv6
[~PE1-segment-routing-ipv6] segment-list list1
[*PE1-segment-routing-ipv6-segment-list-list1] index 5 sid ipv6 2001:DB8:2000::222
[*PE1-segment-routing-ipv6-segment-list-list1] index 10 sid ipv6 2001:DB8:3000::333
[*PE1-segment-routing-ipv6-segment-list-list1] commit
[~PE1-segment-routing-ipv6-segment-list-list1] quit
[~PE1-segment-routing-ipv6] srv6-te-policy locator as1000
[*PE1-segment-routing-ipv6] srv6-te policy policy1 endpoint 2001:DB8:3::3 color 101
[*PE1-segment-routing-ipv6-policy-policy1] binding-sid 2001:DB8:1000::100
[*PE1-segment-routing-ipv6-policy-policy1] candidate-path preference 100
[*PE1-segment-routing-ipv6-policy-policy1-path] segment-list list1
[*PE1-segment-routing-ipv6-policy-policy1-path] commit
[~PE1-segment-routing-ipv6-policy-policy1-path] quit
[~PE1-segment-routing-ipv6-policy-policy1] quit
[~PE1-segment-routing-ipv6] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96
Specify SRv6 End SIDs for the P and PE2 in sequence.
Specify the color and endpoint.
Notes: Configure a segment list.
  Run the system-view command to enter the system view.
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the segment-list list-name command to configure a segment list (an explicit path) for an SRv6 TE Policy candidate path and enter the segment list view.
  Run the index index sid ipv6 ipv6address command to specify a next-hop SID for the segment list.
    You can run the command multiple times. The system generates a SID stack for the segment list by index index in ascending order. If a candidate path in the SRv6 TE Policy is preferentially selected, traffic is forwarded using the segment lists of the candidate path. A maximum of 10 SIDs can be configured for each segment list.
  Run the commit command to commit the configuration.

## Slide 65
Notes: Configure an SRv6 TE Policy.
  Run the system-view command to enter the system view.
  Run the segment-routing ipv6 command to enable SRv6 and enter the SRv6 view.
  Run the srv6-te-policy locator locator-name command to associate a locator with the SRv6 TE Policy to be created. This configuration allows you to specify a binding SID for the SRv6 TE Policy in the locator range.
  Run the srv6-te policy name-value endpoint endpoint-ip color color-value command to create an SRv6 TE Policy and enter the SRv6 TE Policy view.
  (Optional) Run the binding-sid binding-sid command to configure a binding SID for the SRv6 TE Policy.
    The value of binding-sid must be within the range of the static segment specified using the locator locator-name [ ipv6-prefix ipv6-address prefix-length [ static static-length | args args-length ] * ] command.
  Run the candidate-path preference preference command to configure a candidate path and its preference for the SRv6 TE Policy.
    Each SRv6 TE Policy supports multiple candidate paths. A larger preference value indicates a higher candidate path preference. If multiple candidate paths are configured, the one with the highest preference takes effect.
  Run the segment-list list-name [ weight weight-value | path-mtu mtu-value ] * command to configure a segment list for the candidate path of the SRv6 TE Policy.
    The segment list must have been created using the segment-list (SRv6 view) command.
  Run the commit command to commit the configuration.

## Slide 66: L3VPNv4 over SRv6 Policy (5)
Enable the VPN instance IPv4 address family on each PE. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] route-distinguisher 100:1
[*PE1-vpn-instance-vpna-af-ipv4] vpn-target 111:1 both
[*PE1-vpn-instance-vpna-af-ipv4] quit
[*PE1-vpn-instance-vpna] quit
[*PE1-bgp] ipv4-family vpn-instance vpna
[*PE1-bgp-vpna] segment-routing ipv6 traffic-engineer best-effort
[*PE1-bgp-vpna] segment-routing ipv6 locator as1000
[*PE1-bgp-vpna] commit
[~PE1-bgp-vpna] quit
[~PE1-bgp] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 67: L3VPNv4 over SRv6 Policy (6)
Configure a tunnel policy and import VPN traffic. PE1 configurations are as follows: (PE2 configurations are not provided.)
[~PE1] route-policy p1 permit node 10
[*PE1-route-policy] apply extcommunity color 0:101
[*PE1-route-policy] quit
[*PE1] bgp 100
[*PE1-bgp] ipv4-family vpnv4
[*PE1-bgp-af-vpnv4] peer 2001:DB8:3::3 route-policy p1 import
[*PE1-bgp-af-vpnv4] quit
[*PE1-bgp] quit
[*PE1] tunnel-policy p1
[*PE1-tunnel-policy-p1] tunnel select-seq ipv6 srv6-te-policy load-balance-number 1
[*PE1-tunnel-policy-p1] quit
[*PE1] ip vpn-instance vpna
[*PE1-vpn-instance-vpna] ipv4-family
[*PE1-vpn-instance-vpna-af-ipv4] tnl-policy p1
[*PE1-vpn-instance-vpna-af-ipv4] commit
[~PE1-vpn-instance-vpna-af-ipv4] quit
[~PE1-vpn-instance-vpna] quit
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 68: L3VPNv4 over SRv6 Policy (7)
Check SRv6 TE Policy information on PE1.
<PE1>display srv6-te policy
PolicyName : policy1
Color : 101 Endpoint : 2001:DB8:3::3
TunnelId : 1 Binding SID : 2001:DB8:1000::100
TunnelType : SRv6-TE Policy DelayTimerRemain :
Policy State : Up
Admin State : UP Traffic Statistics : Disable
Candidate-path Count : 1
Candidate-path Preference : 100
Path State : Active Path Type : Primary
Protocol-Origin : Configuration(30) Originator : 0, 0.0.0.0
Discriminator : 100 Binding SID : 2001:DB8:1000::100
GroupId : 1 Policy Name : policy1
DelayTimerRemain : - Segment-List Count : 1
Segment-List : list1
Segment-List ID : 1 XcIndex : 1
List State : Up DelayTimerRemain : -
Weight : 1 BFD State : -
SID :
2001:DB8:2000::222
2001:DB8:3000::333
Color of the specified SRv6 Policy
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 69: L3VPNv4 over SRv6 Policy (8)
Check VPNv4 routing information on PE1.
<PE1> display bgp vpnv4 all routing-table 10.1.5.5
BGP local router ID : 10.0.1.1
Local AS number : 100
Total routes of Route Distinguisher(100:1): 1
BGP routing table entry information of 10.1.5.5/32:
Label information (Received/Applied): 3/NULL
From: 2001:DB8:3::3 (10.0.13.3)
Route Duration: 0d00h03m30s
Relay IP Nexthop: FE80::DE99:14FF:FE7A:C301
Relay IP Out-Interface: GigabitEthernet0/3/0.12
Relay Tunnel Out-Interface:
Original nexthop: 2001:DB8:3::3
Qos information : 0x0
Ext-Community: RT <111 : 1>, Color <0 : 101>
Prefix-sid: 2001:DB8:3000::1:0:1E
AS-path 65000, origin incomplete, MED 0, localpref 100, pref-val 0, valid, internal, best, select, pre 255, IGP cost 20
Not advertised to any peer yet
The route recurses to the corresponding SRv6 Policy based on the color attribute.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 70: L3VPNv4 over SRv6 Policy (9)
<CE1>ping -a 10.1.4.4 10.1.5.5
PING 10.1.5.5: 56 data bytes, press CTRL_C to break
Reply from 10.1.5.5: bytes=56 Sequence=1 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=2 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=3 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=4 ttl=254 time=1 ms
Reply from 10.1.5.5: bytes=56 Sequence=5 ttl=254 time=1 ms
Verify the configuration on CE1.
Check vpna's routing information on PE1.
<PE1>display ip routing-table vpn-instance vpna 10.1.5.5 verbose
Routing Table : vpna
Summary Count : 1
Destination: 10.1.5.5/32
Protocol: IBGP Process ID: 0
Preference: 255 Cost: 0
NextHop: 2001:DB8:3::3 Neighbour: 2001:DB8:3::3
State: Active Adv Relied Age: 00h08m38s
Tag: 0 Priority: low
Label: 3 QoSInfo: 0x0
IndirectID: 0x1000174 Instance:
RelayNextHop: :: Interface: policy1
TunnelID: 0x000000003400000001 Flags: RD
The outbound interface is an SRv6 Policy interface.
Configuration roadmap:
Configure interface IPv6 addresses and IS-IS. (Configuration details are not provided.)
Establish an MP-BGP peer relationship between PE1 and PE2.
Enable SR and establish an SRv6 Policy on the backbone network.
Enable the VPN instance IPv4 address family on each PE and establish an MP-IBGP peer relationship between the PEs.
Configure a tunnel policy and import VPN traffic.
Verify the configuration.
PE1
P
PE2
2001:DB88:12::/96
End
2001:DB8:1000::111
Loopback1
10.1.5.5/32
:1
:2
:2
:3
CE1
CE2
Loopback1
10.1.4.4/32
AS 65000
AS 65001
AS 100
10.0.14.0/24
10.0.35.0/24
End
2001:DB8:2000::222
End
2001:DB8:3000::333
2001:DB88:23::/96

## Slide 71
(Short-answer question) An SRv6 SID has 128 bits. What are the three fields of an SRv6 SID?
(Short-answer question) In SIDs corresponding to SRv6 endpoint behaviors, which types of SIDs are similar to the node segments and adjacency segments in SR-MPLS?
Notes: An SRv6 SID has 128 bits and consists of the Locator, Function, and Arguments fields.
End SIDs and End.X SIDs.

## Slide 72
This course describes the concept of SRv6 network programming, SRv6 instruction sets (endpoint node behaviors, source node behaviors, and flavors), SRv6 Policy, and basic SRv6 SID configurations on Huawei NetEngine series routers.
Leveraging the programmability of 128-bit IPv6 addresses, SRv6 enriches the network functions expressed by SRv6 instructions. For example, in addition to identifying an instruction that can indicate a forwarding path, a network function can identify a VAS device, such as a firewall, application acceleration gateway, or user gateway. To deploy a new network function, you only need to define a new instruction, without the need to change the protocol mechanism or deployment.
SRv6 Policy information is carried by extending new NLRIs based on MP-BGP. The controller establishes BGP IPv6 SR Policy peer relationships with forwarders to deliver SRv6 Policies to them.