## Slide 1
Datacom
He Junjian/WX580230
2021.06.09
Shi Miaomiao/WX791350
New

## Slide 2: Huawei CloudWAN Solution Architecture and Fundamentals

## Slide 3
With the rapid development of the Internet industry and the advent of the cloud era, new business models are emerging one after another, and enterprises are moving towards cloudification and digitalization in full swing. Service cloudification brings great flexibility and uncertainty to service applications. As the network scale and complexity continuously grows, O&M complexity increases accordingly. As such, it is imperative for WANs to enter the intelligent cloud-network era.
Huawei's CloudWAN solution is based on advanced network devices and an efficient SDN architecture. This solution aims to build an intent-driven network that is first automated, then self-adaptive, and finally autonomous.
This course describes the architecture of Huawei's CloudWAN solution and the fundamentals of centralized management, control, and analysis provided by the architecture.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the main network management functions of the WAN controller.
  Describe the protocols used for network management and their functions.
  Describe the protocols used for network information collection and reporting.
  Describe the meanings of path constraint parameters.
  Describe the functions of network performance analysis.

## Slide 5
Huawei CloudWAN Solution Overview
Network Management
Network Traffic Control
Network Performance Analysis

## Slide 6: 3 Challenges Facing the WAN in the Cloud Era
Cloudification of millions of enterprises
How can networks be as agile as clouds?
Production service bearer
Can IP provide deterministic experience?
Connection scale x 100 ↑
How can O&M be simpler and networks more reliable?
Public cloud
DC1
DC2
Branch
Branch
Branch
Service deployment time
Dozens of days
< 1 hour
Relay protection
10 ms
One-way delay
200 µs
Two-way delay variation
A failure to meet these requirements may mean a protection failure, incurring accidents.
Train control
10 ms
One-way delay
50 ms
Failover duration
A failure to meet these requirements may mean train out-of-control.
Connection x 100
0 artifact, 0 frame freezing
24/7 online

## Slide 7: CloudWAN: Accelerating the Digital Transformation of Various Industries
SRv6
Slice
Real-time visualization
Fault locating within minutes
iFIT
NETCONF/YANG
Township/outlet
Prefecture/Tier-1 branch
Province/Head office
County/Tier-2 branch
DC
CloudWAN solution advantages:
  Service provisioning within minutes
  Hierarchical slicing for deterministic delay
  Hop-by-hop detection technology for real-time visualization of network-wide status
  ...
CloudWAN solution components
  iMaster NCE-IP: implements centralized management, control, and analysis of the entire network. It enables resource cloudification, full-lifecycle automation, and data analysis-driven intelligent closed-loop management based on business and service intents. Moreover, it provides open network APIs for fast integration with IT systems.
  NetEngine series intelligent routers: adopt the flexible, open, and efficient SDN architecture and provide large capacity and high reliability. They are easy to maintain and energy conserving.

## Slide 8: Intelligent Universal Service Routers for the Cloud Era
NetEngine40E universal service routers
NetEngine 8000
X8
NetEngine 9000 backbone routers
NetEngine 9000-20
NetEngine 9000-8
NetEngine40E-X16A
NetEngine40E-X8A
NetEngine 8000 intelligent routers
NetEngine 8000
X4
NetEngine 8000
M14
NetEngine 8000
M8
NetEngine 8000
M6
NetEngine 8000
F1A
NetEngine 8000
M1A/M1C

## Slide 9: iMaster NCE-IP Architecture and Key Components
NCE, which is based on the cloud architecture, supports distributed deployment on VMs. The overall architecture consists of modules for common services, management, control, and analysis, scenario-specific apps, and northbound and southbound openness.
  Common service module: provides basic network services (such as alarm and log services) and product engineering capabilities (such as disaster recovery and backup).
  Management, control, and analysis module: provides network topology, L2VPN/L3VPN, path computation and optimization, diagnosis, prediction, and other capabilities by module.
  Scenario-specific app module: provides E2E service capabilities, such as agile private lines, for different business scenarios.
  Northbound and southbound openness module: provides northbound APIs and southbound interfaces for quick interconnection or integration with third-party applications, other management and control systems, and devices.
NETCONF
Telnet
SNMP
BGP_LS
PCEP
FTP
Telemetry
Southbound interfaces
Basic services
Public services
Product engineering
Unified cloud-based platform
Value-added apps
Mobile bearer apps
Apps
Unified portal
RESTful
SNMP
XML
CORBA
FTP
Open APIs
Basic apps
Traffic optimization
Service management
NE management
Slice management
Centralized path computation
Southbound programming framework
Manager and Controller
BGP-LS
Analyzer
Anomaly detection
Fault diagnosis
SLA monitoring
Performance analysis
Big data engine

## Slide 10: CloudWAN: Fast Service Provisioning
Simplified, efficient E2E service provisioning within minutes, fast and differentiated service SLA assurance, and 360° graphical display.
IGP domain
Cross-domain
IGP domain
IGP domain
Simplified and efficient: service-driven automatic tunnel creation
E2E optimal: E2E path computation across IGP domains/ASs
Highly reliable: path computation based on link availability/SRLG
SLA assurance: path computation based on bandwidth, delay, etc.
Service
Running status
Layered service topology
Service-related resources
Associated tunnels
Associated alarms
Diagnosis tool
Visualized service display (service 360°)
Template-based rapid service deployment

## Slide 11: CloudWAN: Key Service Assurance with Network Slicing
Slice delivery through NETCONF
Slice 2
(1 Gbit/s)
SRv6/FlexE/iFIT
Slice 1
(2 Gbit/s)
Default slice (5 Gbit/s)
SRv6/FlexE/iFIT
SRv6/FlexE/iFIT
Audio traffic
Video traffic
Default traffic
Slice topology collection through BGP-LS

## Slide 12: CloudWAN: Fast Fault Locating for VPN Services
500
300
0.0001%
100
30
0
10
10
0
Delay (ms)
Jitter (ms)
Packet loss rate
Service 1
Service 2
Service 3
Configuration is required only on the ingress and egress nodes.
Coloring for service identification
Hop-by-hop delay
Packet loss location
Path restoration
Analysis
Telemetry-based data reporting
Terminal
Cloud service

## Slide 13: CloudWAN: Automatic Network Optimization
Real-time network delay monitoring and automatic service path adjustment upon delay deterioration for service experience guarantee.
Delay reporting through BGP-LS
Optimization through PCEP/SR Policy
320 µs
150 µs
50 µs
150 µs
50 µs
50 µs
50 µs
90 µs
PE1
PE2
P3
P1
Delay: 50 µs
Delay: 50 µs
Delay: 320 µs
Delay: 150 µs
Delay: 50 µs
Delay: 90 µs
Delay: 150 µs

## Slide 14: CloudWAN: Network Openness and Programmability
The YANG model can be used for service customization to meet scenario-specific network requirements.
Multi-vendor device management scenario
Multi-vendor network management scenario
Network change scenario
Intent API
NCE-IP
AOC
ISPA
Atomic API
Batch network change processing
AS1
AS2
OSS
Service requirement: network change/O&M self-orchestration
Typical scenario: process customization or batch modification of network parameters
Service model/Service package
Huawei
driver package
Third-party
driver package
….
AS1
AS2
Service requirement: third-party device management
Typical scenario: multi-vendor network
CPE
AOC
NCE-Super
AOC
Manager
Controller
Analyzer
Service requirement: third-party network management
Typical scenario: cloud private line provisioning across a third-party network
NCE-IP
AOC
AS1
AS2
NCE-IP
Notes: In the multi-vendor device management scenario, Huawei provides driver packages. The customer develops or Huawei provides service packages.
In multi-vendor network management scenarios, Huawei provides driver packages, NCE-Super, and Agile Open Container (AOC). AOC interconnects with third-party devices. NCE-Super implements E2E service provisioning through NCE-IP and AOC.
In network change scenarios, AOC provides atomic APIs and network orchestration. The Intelligent Service Process Automation (ISPA) platform orchestrates service processes and provides intent APIs.

## Slide 15
Huawei CloudWAN Solution Overview
Network Management
  Network Management Technologies
  NE Management
  Service Management
Network Traffic Control
Network Performance Analysis

## Slide 16: Network Management Overview for the WAN Controller
Network management, a basic function of the WAN controller, consists of NE management and service management:
  NE management is a basic function of the WAN controller. You can configure basic parameters (such as IP addresses, SNMP, NETCONF, and AAA) on the network devices and controller for them to communicate. In this way, the actual network topology can be displayed on the controller, and functions such as NE configuration management can be implemented in graphical mode.
  Service management is used to configure various underlying tunnels and VPNs carried over these tunnels to provide services for customers.
Controller
R2
R4
R3
R1
Physical networking
R2
R4
R3
R1
Topology display
R2
R4
R3
R1
Service configuration
VRF1
VRF1
Example controller UI

## Slide 17: Network Management Description for the WAN Controller
Network planning and design
Network requirement analysis
Overall network architecture design
Basic network configurations
Global network configuration
IGP
SNMP
NETCONF
…
NE management
NE creation
Data synchronization
Link discovery
Topology management
NE onboarding
Alarm management
Configuration management
…
Service management
Tunnel management:
MPLS TE tunnel
MPLS LDP tunnel
SR-MPLS Policy
SRv6 Policy
VPN management:
L2VPN
L3VPN
EVPN
…
Notes: For details about basic network configuration, see the lab guide.

## Slide 18
Huawei CloudWAN Solution Overview
Network Management
  Network Management Overview
  NE Management
  Service Management
Network Traffic Control
Network Performance Analysis

## Slide 19: Network Management Overview
Scenario description:
  Network device, link, and alarm management for an enterprise's self-built WAN.
Technical protocols:
  SNMP
  NETCONF
  LLDP
Active DC
Standby DC
Branch
Branch
WAN controller

## Slide 20: SNMP
SNMP is deployed for functions such as device alarm and topology management in WAN management.
Simple Network Management Protocol (SNMP) is a network management standard widely used on TCP/IP networks.
SNMP provides a method for managing devices through a network management station (NMS) — a central computer that runs network management software.
By employing the "network management over networks" mode, SNMP implements efficient and batch network device management. In addition, SNMP enables unified management of network devices of different types and from different vendors.
SNMP overview
SNMP
NMS (SNMP server)
e.g.: iMaster NCE
Managed device (SNMP client)
e.g.: router, switch...
Agent process
MIB

## Slide 21: NETCONF
Network Configuration Protocol (NETCONF) is deployed for the controller to deliver configurations, such as VPN instance creation and routing protocol configurations, in WAN management.
SNMP is not a configuration-oriented protocol. On a large-sized network with a complex topology, SNMP cannot meet network management requirements, especially the configuration management requirements.
SNMP's drawbacks
NETCONF
NMS (NETCONF server)
e.g.: iMaster NCE
Managed device (NETCONF client)
e.g.: router, switch...
NETCONF provides a mechanism for the NMS to communicate with network devices.
To be specific, the network administrator can use this mechanism to add, modify, and delete the configurations of network devices as well as obtain the configurations and status of network devices.
NETCONF is based on the Extensible Markup Language (XML).
NETCONF

## Slide 22: LLDP
Link Layer Discovery Protocol (LLDP) is defined in IEEE 802.1ab. It can identify the interfaces on devices and provide information about connections between devices. LLDP can also discover the paths between clients, switches, routers, application servers, and network servers.
Devices use LLDP to collect their physical connection information and SNMP to report collected information to the controller, which then automatically discovers links.
R1
R2
GE0/0/1
GE0/0/1
Controller
LLDP
SNMP
R1
R2
GE0/0/1
GE0/0/1

## Slide 23: NE Management
After synchronizing basic data from NEs, the controller can perform the following operations:
  Creates NEs one by one or in batches.
  Synchronizes NE data to the controller database.
  Discovers links and displays physical connections. Manual link addition is also supported.
  Configures NE information, such as interface IP addresses and router IDs.
  Manages alarms and displays alarm information.
NE management
NE creation
Data synchronization
Link discovery
Alarm management
NE configuration
...

## Slide 24
Huawei CloudWAN Solution Overview
Network Management
  Network Management Overview
  NE Management
  Service Management
Network Traffic Control
Network Performance Analysis

## Slide 25: Tunnel Management Overview
The controller uses the following protocols for tunnel management:
  IGP: generates network topology information, such as bandwidth, delay, and SID information, on a router.
  BGP-LS: collects topology information and reports collected information to the controller. If an RR exists on the network, you only need to deploy BGP-LS on the RR and establish a BGP-LS peer relationship between the RR and controller.
  Path Computation Element Communication Protocol (PCEP): exchanges information between the controller and forwarders. For example, Huawei's CloudWAN solution uses PCEP to monitor tunnel status.
  NETCONF: delivers tunnel configurations from the controller to forwarders.
  BGP SR Policy: establishes BGP SR Policy peer relationships between the controller and PEs, so that the controller can deliver SR Policies through BGP peer relationships to instruct forwarders to forward packets. To reduce the number of peer relationships, you can deploy an RR and configure PEs and the controller to function as RR clients.
R2
R4
R3
Controller
R1
IGP
PCEP/NETCONF/BGP-LS/BGP SR Policy

## Slide 26: Topology Information Generation by Routers
The key information that needs to be advertised for SR-MPLS tunnels is as follows:
  SID: node SID, adjacency SID, and prefix SID
  SRGB: a set of user-specified global labels reserved for SR-MPLS
  Interface bandwidth information: physical bandwidth and reservable bandwidth
  Interface delay information
R2
R4
R3
R1
SR-MPLS
The key information that needs to be advertised for SRv6-based tunnels is as follows:
  SID: END SID and END.X SID
  Locator: After a locator value is configured for a node, the system generates a locator route and propagates the route throughout the SR domain using an IGP. Other nodes on the network can locate this node through the locator route.
  Interface bandwidth information: physical bandwidth and reservable bandwidth
  Interface delay information
R2
R4
R3
R1
SRv6
BGP-LS
BGP SR Policy
PCEP

## Slide 27: Topology Information Collection by BGP-LS
R2
Controller
BGP-LS peer relationship
R1
IGP
This has high requirements on the computing capability of the upper-layer controller. In addition, the controller must support the IGP and its algorithms. When cross-IGP domain topology information is collected, the upper-layer controller cannot obtain complete topology information and therefore cannot compute optimal E2E paths. When different routing protocols send topology information to the controller, the controller analyzes and processes the topology information in a complex manner.
Drawbacks of direct topology information collection through an IGP by the controller
The topology information discovered by IGPs is summarized and reported to an upper-layer controller through BGP. With powerful routing capabilities of BGP, BGP-LS has the following advantages:
  Lowers the requirements on the controller's computing and IGP capabilities.
  Facilitates path selection and computation on the controller by using BGP to summarize topology information in each process or AS and report the complete information directly to the controller.
  Requires only one routing protocol (BGP) to report information about the entire network's topology to the controller.
BGP-LS
BGP-LS
BGP SR Policy
PCEP

## Slide 28: Topology Information Reporting to the Controller Through BGP-LS
Each router maintains one or more LSDBs. The LSDB contains multiple link attributes, such as the interface IP address, link metric, TE metric, link bandwidth, and reservable bandwidth. The BGP process of a router obtains information from these LSDBs and carries the information in the extended NLRI attribute.
R2's LSDB
R1 link state information
R2 link state information
R3 link state information
R4 link state information
R2's BGP process
R1 link state information
R2 link state information
R3 link state information
R4 link state information
Extracting
Node NLRI
NLRI
Link NLRI
Topology Prefix NLRI
(IPv4)
Topology Prefix NLRI
(IPv6)
Reporting
Controller
Advertised to the BGP-LS peer
BGP-LS
BGP SR Policy
PCEP

## Slide 29: PCEP Overview
Path Computation Element (PCE) can compute network paths or routing entities (components, applications, or network nodes) based on the network topology. A path computation client (PCC) is any client or application that requests path computation from a PCE. PCEP defines communication between the PCC and PCE and between two PCEs (RFC 5440).
PCEP is a TCP-based protocol defined by the IETF PCE working group. It defines a group of messages and objects for PCEP session management, including TE LSP reporting and path delivery. PCEP provides a mechanism for the PCE to compute LSP paths for PCCs. In PCEP interaction, PCCs send LSP state reports to the PCE, and the PCE sends LSP path update instructions to PCCs.
BGP-LS
BGP SR Policy
PCEP
R2
PCC
Controller
PCE
Path delivery
Path computation
LSP state reporting
Notes: For more information, visit https://datatracker.ietf.org/doc/rfc5440.

## Slide 30: Tunnel Path Computation by PCEP
A TCP-based PCEP session connects a PCC to a PCE. A PCC initiates a PCEP session and establishes a connection with a PCE. During session establishment, the PCC and PCE negotiate session capabilities. After a PCEP session is established, the PCC sends LSP state updates to the PCE. Upon receipt of LSP state updates, the PCE computes paths for LSPs that have path constraint changes as well as LSPs that do not have paths and instructs the PCC to update LSP paths. After a PCEP session is torn down, the TCP connection is immediately closed, and the PCC attempts to re-establish a PCEP session.
PCEP provides the following functions:
  Allows the PCC to delegate LSP control to the PCE. The PCE needs to synchronize LSP state information from the PCC.
  Allows the PCE to compute paths based on delegated LSPs' attributes, including the bandwidth, explicit path, priority, and affinity attributes.
  Transmits computed LSP attributes from the PCE to the PCC, which reports information about new LSPs to the PCE after updating paths.
BGP-LS
BGP SR Policy
PCEP
PCC
PCE
TCP connection
TEDB
Session negotiation
Session establishment
Session holding
Tunnel delegation
LSP path update
PCEP is used for tunnel delegation in Huawei's CloudWAN solutions.

## Slide 31: BGP SR Policy Overview
According to RFC 8402, an SR Policy is an ordered list of segments. In addition, it defines a framework for SR technologies used to provide functions such as computing/generating/maintaining the segment list and steering traffic.
After an SR Policy peer relationship is established between the controller and PE, the controller delivers the computed path to the ingress of the SR Policy.
For example, after R1 establishes an SR Policy peer relationship with the controller, if the path of the tunnel to be created is R1-R2-R3, the controller can deliver the path information together with the color attribute to R1 for subsequent data packet forwarding.
R2
R4
R3
Controller
R1
IGP
BGP SR Policy peer relationship
Forwarding path delivery (R1-R2-R3)
BGP-LS
BGP SR Policy
PCEP

## Slide 32: Tunnel Management Instance on the Controller
To facilitate configuration, the controller provides the following functions:
  Directly creates a bidirectional tunnel between the ingress and egress.
  Allows you to configure tunnel templates and color templates to simplify the configuration of some parameters.
In Huawei's CloudWAN solution:
  The SR-MPLS TE tunnel configurations are delivered by NETCONF, and the tunnel status is reported by PCEP.
  The SR-MPLS Policy configurations are delivered by BGP SR Policy, and the tunnel status is reported by BGP-LS.
  The SRv6 Policy configurations are delivered by BGP SR Policy, and the tunnel status is reported by BGP-LS.
Tunnel management
SR-MPLS TE
SR-MPLS Policy
SRv6 Policy
Notes: The controller supports static configuration of various tunnels. Static tunnels are rarely used on live networks and are therefore not described in this course.

## Slide 33: SR-MPLS TE Tunnel Creation (1)
Optional constraints:
  Bandwidth constraint: ensures that the bandwidth configured for a service does not exceed the remaining bandwidth of the link that the service traverses.
  PIR constraint: ensures that the peak bandwidth does not exceed the BC0 bandwidth of the link that the service traverses. PIR refers to the peak bandwidth of a service.
  Delay limit constraint: ensures that the path delay of a service does not exceed the configured delay limit.
  Hop limit constraint: ensures that the number of links that a service traverses does not exceed the configured hop limit.
  Affinity constraint: determines which types of links are allowed and which types of links are not allowed for services.
  Primary-backup path disjoint constraint: ensures that the PCE algorithm computes primary and backup paths that are as disjoint as possible in tunnel hot standby scenarios. The primary and backup paths are separated based on SRLG, node, and link information in sequence.
R2
R4
R3
R1
IGP
1000 Mbit/s
1000 Mbit/s
1000 Mbit/s
500 Mbit/s
SR-MPLS TE
SRv6 Policy
SR-MPLS Policy

## Slide 34: SR-MPLS TE Tunnel Creation (2)
With the path computation algorithm, the controller can provide the following path computation results if the constraints are met:
  Least cost: path with the least cost among all paths that meet the constraint
  Minimum delay: path with the minimum delay among all paths that meet the constraint
  Bandwidth balancing: path with the most remaining bandwidth among all paths that meet the constraint and have the same cost
In this example, the least cost constraint is selected, the ingress is R1, and the egress is R3. Given this, the forward path computed by the controller is R1-R2-R3, and the reverse path is R3-R2-R1.
In Huawei's CloudWAN solution, the controller uses NETCONF to deliver tunnel configurations, and R1 and R3 report tunnel status through PCEP.
To facilitate configuration and deployment, the controller provides templates. When creating a tunnel, you can skip the configuration of some parameters by selecting a template.
R2
R4
R3
R1
IGP
1000 Mbit/s
1000 Mbit/s
1000 Mbit/s
500 M
Controller
NETCONF/PCEP
Cost=100
Cost=100
Cost=100
Cost=200
SR-MPLS TE
SRv6 Policy
SR-MPLS Policy

## Slide 35: SR-MPLS Policy Creation
The tunnel constraints and path computation algorithm of SR-MPLS Policies are similar to those of SR-MPLS TE tunnels.
When creating an SR-MPLS Policy, you need to specify the color for each tunnel. In this example, the color name is test, the maximum delay is 10 ms, and the color ID is automatically generated by the controller.
One SR-MPLS Policy can contain multiple candidate paths. Multiple segment lists can be configured for each candidate path to implement load balancing.
In this example, the single-candidate-path single-segment-list mode is used. The forward and reverse traffic must pass through R2.
In Huawei's CloudWAN solution, the SR-MPLS Policy configurations are delivered through BGP SR Policy, and R1 and R3 use BGP-LS to report tunnel status.
R2
R4
R3
R1
IGP
3 ms
3 ms
10 ms
10 ms
Controller
Color name: test
Max. delay: 10 ms
Explicit node R2
Explicit node R2
BGP SR Policy/BGP-LS
SR-MPLS TE
SRv6 Policy
SR-MPLS Policy

## Slide 36: SRv6 Policy Tunnel Creation: Single Candidate Path and Multiple Segment Lists
The tunnel constraints and path computation algorithm of SRv6 Policies are similar to those of SR-MPLS TE tunnels.
When creating an SRv6 Policy, you need to specify the color for each tunnel. In this example, the color name is test, and the color ID is automatically generated by the controller.
An SRv6 Policy can contain multiple candidate paths with the preference attribute. The valid candidate path with the highest preference functions as the primary path of the SRv6 Policy, and the valid candidate path with the second highest preference functions as a backup path. Multiple segment lists can be configured for each candidate path to implement load balancing.
In this example, the single-candidate-path multi-segment-list mode is used. R2 is the explicit node for path 1, and R4 is the explicit node for path 2.
In Huawei's CloudWAN solution, the SR-MPLS Policy configurations are delivered through SRv6 Policy, and R1 and R3 use BGP-LS to report tunnel status.
R2
R4
R3
R1
IGP
Controller
Color name: test
SL1: R2 (explicit node)
SL2: R4 (explicit node)
BGP SR Policy/BGP-LS
3 ms
3 ms
10 ms
10 ms
SR-MPLS TE
SRv6 Policy
SR-MPLS Policy

## Slide 37: SRv6 Policy Group
SRv6 Policy group: allows a group of tunnels that share the same SLA requirements to be quickly established.
Application scenario: Multiple SRv6 Policies need to be established in batches before service creation. The available tunnel types are as follows:
  Any-to-any: indicates that a full-mesh network is established between NEs.
  Hub-spoke: indicates that an NE is either a hub or spoke node. Communication between all spoke nodes must be implemented through the hub node.
In Huawei's CloudWAN solution, the SRv6 Policy group is used in tunnel planning scenarios. Specifically, tunnel paths are computed in advance and delivered upon service request.
R2
R4
R3
R1
Any-to-any
R2 Hub
R4 Spoke
R3 Spoke
R1 Spoke
Hub Spoke

## Slide 38: Network Slice-based Tunnel Creation
Essentially, network slicing logically divides a physical network into multiple virtual E2E networks. As such, a specific network slice can then be selected when a tunnel is created.
A network slice is deployed as follows:
  Slice creation: Set the slice type.
  Link addition: Select the links on which the slice is to be created.
  Slice deployment: Deliver slice configurations, such as bandwidth, to devices for slice link generation.
  Slice activation: Configure IP addresses for both ends of the slice link and configure data, such as IGP parameters, to achieve E2E connectivity at the network layer.
  Tunnel creation: Select the specified slice during tunnel creation.
Slice creation
Link addition
Slice deployment
Slice activation
SR-MPLS TE
SR-MPLS Policy
SRv6 Policy

## Slide 39: VPN and Tunnel Binding
The following types of VPNs are available in enterprise network scenarios:
  L2VPN: The customer IP addresses are on the same network segment.
  L3VPN: The customer IP addresses are on different network segments.
  EVPN: The customer IP addresses are either on the same network segment or on different network segments.
A tunnel policy is used by an application module to select tunnels for VPN services. There are two types of tunnel policies:
  Tunnel type prioritizing policy: recurses a service to tunnels based on the tunnel type priority and the number of tunnels participating in load balancing (preferred mode).
  Tunnel binding policy: binds a destination address to a tunnel, so that the traffic of VPN services referencing the policy will be transmitted over the bound tunnel.
A VPN service first selects tunnels in the up state based on the tunnel policy, and then selects a forwarding path from tunnels that meet the requirements.
L2VPN
L3VPN
EVPN
Auto selection
Color
DSCP
SR-MPLS TE
SR-MPLS Policy
SRv6 Policy
SRv6 Policy group
Tunnel policy-based tunnel type selection
A forwarding path is selected among tunnels of the same type in any of the following modes:

## Slide 40: L3VPN over SR-MPLS TE: Automatic Tunnel Selection
CE1 searches the routing table and forwards the packet to R1.
R1 searches the VPN routing table, adds the label allocated by R3 to the corresponding VPN instance to the packet, selects an SR-MPLS TE tunnel based on the tunnel policy, and adds a tunnel label to the packet.
After receiving the packet, R2 swaps the outer label and forwards the packet to R3.
After receiving the packet, R3 removes the outer label and forwards the packet to CE2 based on the inner label. The packet then reaches CE2.
R2
R1
R3
SR-MPLS TE
CE1
CE2
Ingress: CE1
Egress: CE2
Ingress: CE1
Egress: CE2
VPN label
LSP label 1
Ingress: CE1
Egress: CE2
VPN label
LSP label 2
Ingress: CE1
Egress: CE2
1
2
3
4

## Slide 41: L3VPN over SRv6 Policy: Color-based Traffic Diversion
CE1 searches the routing table and forwards the packet to R1.
R1 searches the VPN routing table and adds the END.DT4 SID (F30::30) allocated by R3 to the corresponding VPN instance to the packet. After finding that the corresponding route carries the color attribute of 100, R1 selects an SRv6 Policy tunnel with the color attribute being 100 based on the tunnel policy and adds a tunnel label to the packet. In this example, the forwarding path specified for the SRv6 Policy is R1-R2-R3.
After receiving the packet, R2 changes the destination IPv6 address to FC03::3, decrements the SL value by 1, and forwards the packet to R3.
After receiving the packet, R3 decrements the SL value by 1 and finds that FC30::30 is the SID locally assigned to CE2. R3 then removes the IPv6 header and sends the packet to CE2.
R2
R1
R3
SRv6 Policy Color 100
CE1
CE2
Ingress: CE1
Egress: CE2
Ingress: CE1
Egress: CE2
Ingress: CE1
Egress: CE2
1
2
4
F30::30
FC03::3
FC02::2
SL=2
IPv6 header
Ingress: CE1
Egress: CE2
3
F30::30
FC03::3
FC02::2
SL=1
IPv6 header
FC01::1
FC02::2
F30::30
FC03::3

## Slide 42: L3VPN over SRv6 Policy: DSCP-based Traffic Diversion
DSCP-based traffic diversion is more flexible than color-based traffic diversion, as it allows traffic of the same VPN customer but with different priorities to enter different SRv6 Policies.
  CE1 searches the routing table and forwards the packet with DSCP 46 to R1.
  R1 searches the VPN routing table and adds an END.DT4 SID (F30::30) allocated by R3 to the corresponding VPN instance to the packet. R1 then maps DSCP 46 to color 100, selects an SRv6 Policy with color 100 based on the tunnel policy, and adds a tunnel label to the packet. In this example, the forwarding path specified for the SRv6 Policy is R1-R2-R3.
  After receiving the packet, R2 changes the destination IPv6 address to FC03::3, decrements the SL value by 1, and forwards the packet to R3.
  After receiving the packet, R3 decrements the SL value by 1 and finds that FC30::30 is the SID locally assigned to CE2. R3 then removes the IPv6 header and sends the packet to CE2.
DSCP-based traffic diversion is more suitable for scenarios where there are multiple paths to the same destination and high-quality links need to be selected for services with high requirements.
R2
R1
R3
SRv6 Policy Color 100
CE1
CE2
Ingress: CE1
Egress: CE2
Ingress: CE1
Egress: CE2
1
4
DSCP: 46
DSCP: 46
Color: 100
SRv6 Policy
FC01::1
FC02::2
F30::30
FC03::3
Ingress: CE1
Egress: CE2
2
F30::30
FC03::3
FC02::2
SL=2
IPv6 header
Ingress: CE1
Egress: CE2
3
F30::30
FC03::3
FC02::2
SL=1
IPv6 header
DSCP-based traffic diversion can implement differentiated services for the same VPN customer.

## Slide 43
(Multiple-answer question) Which of the following protocols are used for communication between the controller and NEs?( )
  PCEP
  SNMP
  NETCONF
  BGP-LS
(True or False) In Huawei's CloudWAN solution, PCEP is used to deliver path information computed by the controller to forwarders.( )
Notes: ABCD
False

## Slide 44
The prerequisite for the controller to perform network management is that the NEs and controller are reachable to each other at the IP layer. Basic interconnection parameters, such as IGP, SNMP, and NETCONF parameters, need to be configured on the controller and forwarders, so that the controller can manage these NEs.
Compared with traditional CLI-based service management, controller-based service management has obvious advantages. The controller computes tunnel paths and uses NETCONF or BGP SR Policy to deliver information to forwarders. The controller uses NETCONF to deliver VPN information to forwarders, which select tunnels based on tunnel policies during data forwarding.
In addition to NE management and service management, the controller also provides functions such as alarm management, which will be described in the following sections.

## Slide 45
Huawei CloudWAN Solution Overview
Network Management
Network Traffic Control
  Network Flow Control Technologies
  Network Information Collection
  Route Optimization
Network Performance Analysis

## Slide 46: Analysis on Network Traffic Control Requirements for the WAN Controller
As enterprises move towards digital transformation, the WAN calls for new traffic control technologies in the cloud era.
Inconsistent across domains
  IGP TE can flood only the topology information of the IGP area where it resides, and cannot compute or establish an E2E TE tunnel across IGP areas or ASs.
  The traditional path computation algorithm can only be determined by the ingress of a tunnel. As a result, collaborative management cannot be achieved, and network bandwidth resources cannot be optimized in a coordinated manner.
Resource preemption
  When resources are insufficient, high-priority tunnels preempt the resources of low-priority tunnels.
Difficult planning
  When a network is large, manual path planning is difficult.
MPLS TE drawbacks
Topology processing for centralized path computation
  Collects topology information from multiple areas, combines and processes collected topology information, and computes paths based on the global topology across domains.
Multi-constraint-based path computation
  Provides the ability to optimize traffic based on multiple constraints, such as path locking, candidate path, and affinity attributes.
What-you-see-is-what-you-get
  Provides multiple path computation policies and intelligently plans service paths.
Computation of multiple types of tunnel paths
  Computes paths for multiple types of tunnels, such as MPLS TE tunnels, SR-MPLS TE tunnels, SR-MPLS Policies, and SRv6 Policies.
Traffic control requirements for the controller

## Slide 47: Traffic Control Process Overview of the WAN Controller
The traffic control technology of the WAN controller provides E2E optimal path computation and optimization services. It allows you to perform centralized configuration and management of network topology information and tunnel constraints to optimize network bandwidth utilization and maximize the utilization of network resources.
Traffic control can be divided into three phases: network information collection, path computation for network traffic optimization, and optimization result delivery.
1. Network information collection
The controller collects global network information, including:
Network topology
Network bandwidth
Link delay
Network traffic and other information
2. Path computation for network traffic optimization
The controller computes paths based on the optimization target. Optimization targets include:
Least path cost
Shortest path delay
...
3. Optimization result delivery
The controller delivers the computation result to network devices in any of the following modes:
NETCONF
BGP SR Policy ...

## Slide 48
Huawei CloudWAN Solution Overview
Network Management
Network Traffic Control
  Network Traffic Control Overview
  Network Information Collection
  Path Optimization
Network Performance Analysis

## Slide 49: Topology Information and Interface Bandwidth Collection
The controller uses BGP-LS to collect topology and interface bandwidth information from routers.
  Forwarders run an IGP (such as IS-IS) to advertise topology and bandwidth information.
  One of the forwarders, for example, P1, establishes a BGP-LS peer relationship with the controller.
  The controller processes topology information based on the node and link information reported by BGP-LS.
Controller
PE1
P1
P2
PE2
PE3
P3
P4
PE4
IGP link
BGP-LS
Topology/Bandwidth
20 Mbit/s
50 Mbit/s
80 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s
100 Mbit/s

## Slide 50: Link Delay Collection
Link delay information can be collected in either static or dynamic mode.
  In static mode, link delay is obtained through other means and then manually entered on the NCE-IP UI. Alternatively, link delay can be configured using commands on routers and then flooded in the IGP domain.
  In dynamic mode, a router detects the link delay in real time through a detection protocol and reports the link delay to the controller.
Compared with the static mode, the dynamic mode can reflect the link delay status in real time and is more suitable for scenarios where delay needs to be guaranteed. This section describes dynamic delay collection.
The dynamic link delay is collected using TWAMP, flooded in the IGP domain, and then reported to the controller through BGP-LS.
Controller
PE1
P1
P2
PE2
PE3
P3
P4
PE4
IGP link
BGP-LS
Delay
2 ms
5 ms
8 ms
10 ms
100 ms
10 ms
10 ms
10 ms
10 ms
10 ms

## Slide 51: Traffic Statistics Collection
To determine bandwidth sufficiency and perform optimization, the controller needs to collect interface and tunnel traffic statistics in real time:
  SNMP: reports information such as the interface traffic rate and bandwidth usage within minutes.
  Telemetry: reports interface traffic information and tunnel traffic statistics within seconds.
Ps need to report interface traffic statistics, and PEs need to report both interface and tunnel traffic statistics.
Controller
PE1
PE2
PE3
P3
P4
PE4
Interface and tunnel traffic statistics
Interface traffic statistics
Delay
P1
P2

## Slide 52
Huawei CloudWAN Solution Overview
Network Management
Network Traffic Control
  Network Traffic Control Overview
  Network Information Collection
  Path Optimization
Network Performance Analysis

## Slide 53: Network Optimization Constraint Parameters and Optimization Policies
Optimization policies:
  Least cost: selects a path with the least cost among all paths that meet the specified constraints.
  Minimum delay: selects a path with the minimum delay among all paths that meet the specified constraints.
  Availability+least cost: selects a path with the maximum link availability and least cost among all paths that meet the specified constraints.
  Availability+minimum delay: selects a path with the maximum link availability and minimum delay among all paths that meet the specified constraints.
Constraint | Description
Priority | This constraint specifies the priorities of different types of tunnels and enables a tunnel with a higher priority to preempt the bandwidth resources of a tunnel with a lower priority.
Bandwidth | This constraint requires paths to be computed based on tunnel bandwidth requirements.
Hop count | This constraint requires paths to be computed based on hop count requirements. For example, the path length of an SR-TE tunnel is limited by the maximum stack depth (MSD) of the ingress node.
Explicit path | This constraint requires paths to be computed in either strict or loose mode. You can specify the links or nodes that are to be included or excluded.
Delay threshold | This constraint requires paths to be computed within the threshold range specified for path computation.
Affinity | This constraint supports the include-all, include-any, and exclude modes.
Notes: Bandwidth-balancing path: indicates the path with more remaining bandwidth among all paths that meet constraints and have the same cost.
Maximum availability path: indicates the path with the maximum availability among all paths that meet the constraint.

## Slide 54: Overview of Controller-based Optimization
Generally speaking, optimization is to optimize service paths (LSPs). LSPs are logical paths and can be considered as tunnels, whereas links are physical paths. One link can carry multiple tunnels, and each tunnel (LSP) corresponds to a service. Therefore, service paths can be changed based on either links or tunnels:
  Link optimization: When one or more links are selected for optimization, all LSPs carried by the selected links are involved in path computation.
  Tunnel optimization: When one or more tunnels are selected for optimization, the LSPs corresponding to the selected tunnels are involved in path computation.
The optimization solution supports both automatic and manual optimization:
  In an automatic optimization scenario, traffic is automatically analyzed, and the optimization is automatically performed at scheduled times.
  In a manual optimization scenario, traffic is manually optimized on demand based on network conditions.
According to the optimization scope, optimization can be classified into the following two types:
  Local optimization: optimizes specified tunnels or links.
  Global optimization: optimizes all tunnels or links.
Network optimization
Link optimization
Tunnel Optimization
Automatic optimization
Manual optimization
Global optimization
Local optimization
Notes: The link availability is calculated based on the ratio of the time when the link is normal to the total statistical time.

## Slide 55: Example for Optimizing a Single Tunnel (Based on the Least Cost Policy)
An SRv6 Policy tunnel is established between PE1 and PE4. As services increase, the bandwidth usage of the link between P1 and P2 reaches 80%, which exceeds the preset optimization threshold 60%. In this case, some service traffic needs to be diverted to other links.
Before optimization, the path is PE1-P1-P2-PE2-PE4.
Path optimization is performed based on the least cost policy.
After optimization, the path is PE1-PE3-P3-P4-PE4.
PE1
P1
P2
PE2
PE3
P3
P4
PE4
20
50
80
100
100
100
100
100
100
100
Service
PE1
P1
P2
PE2
PE3
P3
P4
PE4
20
50
80
100
100
100
100
100
100
100
Service
Before optimization
After optimization
usage：80%

## Slide 56: Example for Optimizing a Single Tunnel (Based on the Minimum Delay Policy)
An SRv6 Policy tunnel is established between PE1 and PE4. The service monitoring result shows that the delay of the service carried by the tunnel is too long. Therefore, the service path needs to be adjusted to reduce the network delay.
Before optimization, the path is PE1-PE3-P3-P4-PE4.
Path optimization is performed based on the minimum delay policy.
After optimization, the path is PE1-P1-P2-PE2-PE4.
PE1
P1
P2
PE2
PE3
P3
P4
PE4
Service
PE1
P1
P2
PE2
PE3
P3
P4
PE4
5 ms
3 ms
5 ms
5 ms
10 ms
10 ms
10 ms
2 ms
2 ms
5 ms
Service
5 ms
3 ms
5 ms
5 ms
10 ms
10 ms
10 ms
2 ms
2 ms
5 ms
Before optimization
After optimization

## Slide 57: Example for Optimizing a Single Link (Maintenance State Setting)
An SRv6 Policy tunnel is established between PE1 and PE4. The optical module connecting P1 to P2 is unstable and needs to be replaced.
Before optimization, the path is PE1-P1-P2-PE2-PE4.
Set the link between P1 and P2 to the maintenance state to prevent the replacement from affecting services.
After optimization, the path is PE1-PE3-P3-P4-PE4 (minimum delay).
PE1
P1
P2
PE2
PE3
P3
P4
PE4
Service
Link for maintenance
PE1
P1
P2
PE2
PE3
P3
P4
PE4
Service
Link for maintenance
Before optimization
After optimization
5 ms
3 ms
5 ms
5 ms
10 ms
10 ms
10 ms
2 ms
2 ms
5 ms
5 ms
3 ms
5 ms
5 ms
10 ms
10 ms
10 ms
2 ms
2 ms
5 ms

## Slide 58: Controller-based Multi-tunnel Optimization from the Global Perspective
There are two tunnels between PE1 and PE2 that carry different services. As the service traffic increases, the bandwidth usage of the tunnel exceeds the threshold.
Before traffic optimization, two service flows pass through the same path PE1-PE1-P2-PE2
Service 1 has a higher priority and is optimized from the global perspective by the controller.
After optimization, the path of service 1 is PE1-P1-P2-PE2, and that of service 2 is PE3-P3-P4-PE4-PE2.
PE1
P1
P2
PE2
PE3
P3
P4
PE4
20
50
80
100
100
100
100
100
100
100
Service 1
Service 2
PE1
P1
P2
PE2
PE3
P3
P4
PE4
20
50
80
100
100
100
100
100
100
100
Service 1
Service 2
Before optimization
After optimization

## Slide 59: MBB-enabled Zero Packet Loss During Tunnel Path Switching
The make-before-break (MBB) mechanism ensures that the original path is deleted after a new forwarding path is established. During this period, traffic is still forwarded along the original path. The system deletes the original path only after the switch-delay timer expires. This prevents traffic interruption caused by path switching.
R2
R4
R3
R1
Original path
New path
The controller delivers the new path (R1-R4-R3) to the forwarder R1.
R1 starts to establish a new path and starts the switch-delay timer.
After the switch-delay timer expires, R1 forwards traffic along the new path.
Controller
1
2
3

## Slide 60
(Multiple-answer question) Which of the following traffic optimization policies are supported by the controller? ( )
  Least cost
  Minimum delay
  Availability+least cost
  Availability+minimum delay
Notes: ABCD

## Slide 61
A tunnel is established based on multiple constraints, such as the explicit path and affinity attributes. However, as the number of services increases, situations such as tunnel congestion, excessive delay, and high bandwidth usage may arise. In this case, you can re-optimize the entire traffic path through the controller from a global perspective.
Tunnels still need to meet basic tunnel constraints during path optimization. When the network is large, manual tunnel optimization is difficult, highlighting the advantage of automatic optimization by the controller.

## Slide 62
Huawei CloudWAN Solution Overview
Network Management
Network Traffic Control
Network Performance Analysis

## Slide 63: Classification and Process of Network Performance Analysis
Network performance analysis is classified into the following types:
  IP performance analysis
    Network traffic analysis: processes and analyzes the collected network traffic data and displays traffic data in multiple modes, such as reports, dashboards, topologies, and maps, for data visualization.
    Network quality analysis: collects performance data such as link bandwidth, delay, jitter, and packet loss, and displays link quality for quick locating of links with deteriorated quality.
  VPN service analysis: detects service quality through iFIT in-band measurement in real time and quickly identifies private line service faults, so that the faults can be located and rectified in a timely manner.
Interconnection between Analyzer and Manager
Basic performance configuration operations
(Manager)
Configuration of automatic performance monitoring
Inventory configuration
Threshold configuration
Configuration of TWAMP/ICMP quality monitoring schemes
Quality path restoration and fault diagnosis
VPN service analysis and assurance
Configuration of iFIT monitoring
IP performance analysis
IP quality analysis
VPN service analysis

## Slide 64: Overview of Controller Traffic Analysis Functions
Performance monitoring: Performance monitoring instances are the basis of traffic analysis and provide data sources for analysis.
Inventory synchronization: This function synchronizes resource information, such as NE, board, port, link, and ring information, from Manager to Analyzer. You can create a synchronization task and set a period to periodically synchronize inventory information.
Performance overview: The controller displays performance data from different dimensions on different home pages for management.
Performance report: The controller provides various performance report-related functions, such as displaying performance reports by time range, sorting report data in ascending or descending order, filtering report data, customizing report headings, and customizing the number of data records to be displayed on each page of a report.
Performance topology: The IP performance topology reflects the networking and running status of devices. You can monitor the running status of the entire network in real time by viewing the color and status of device icons in the topology view.
Intelligent analysis: The controller predicts the future resource status based on the current resource status.
Traffic Analysis
Quality Analysis
VPN Service Analysis
Traffic analysis
Performance monitoring
Inventory data synchronization
Performance overview
Performance report
Performance topology
Intelligent Analysis
...

## Slide 65: Analyzer obtains inventory data from Manager.
If you want to use the performance topology and traffic monitoring functions, you need to synchronize the inventory data of related resources.
After obtaining all inventory data, Analyzer performs background processing on the data and displays task details on the foreground.
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 66: Performance Reports
The NCE solution provides various types of reports to help users learn performance data, such as network-wide resource status and port, link, and ring traffic. Users can view reports to evaluate the current network status. This effectively supports O&M and capacity expansion.
Layer 2 link traffic report
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 67: Telemetry Deployment
Telemetry, which has advantages such as large application scope and short collection period, is suitable for large-scale network O&M.
Static subscription: Devices function as gRPC/UDP clients and periodically report data based on the collection subscription configuration. Analyzer functions as the gRPC/UDP server, receives and processes data reported by devices, and provides an entry for users to query historical performance data.
Dynamic subscription: Devices function as gRPC servers, and Analyzer functions as a gRPC client to proactively query the real-time performance data of devices. The devices return real-time performance data based on the query configuration. Analyzer provides a unified entry for users to query real-time performance data.
Traffic Analysis
Quality Analysis
VPN Service Analysis
Notes: SNMP supports real-time performance data collection at an interval of 5s, 10s, or 15s, but not 1s.

## Slide 68: Telemetry Traffic Statistics Reporting
Historical traffic data display
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 69: TWAMP Deployment
TWAMP threshold configuration: During a TWAMP test, you need to set different levels of alarm thresholds for different indicators of different resources. If the indicator value generated by the network or service exceeds the set threshold, an alarm is triggered for quick fault locating.
TWAMP test task deployment: TWAMP test tasks are deployed to monitor E2E network service quality and help O&M personnel quickly demarcate and locate faults.
TWAMP performance reports: By viewing TWAMP performance reports, you can intuitively learn the information and quality of each service and discover services that require special attention.
Indicator | Description
Two-way packet loss rate | Rate of lost packets to transmitted packets on a link within a period.
Two-way delay | Duration from when the source end sends a packet to the destination end to when the source end receives an acknowledgment packet from the destination end.
Two-way jitter | Difference between the two-way delays of two adjacent packets with the same destination.
One-way packet loss rate | Rate of lost packets to transmitted packets on a link within a period in the source-to-destination or destination-to-source direction.
One-way delay | Duration from when the source end sends a packet to when the destination end receives the packet or from when the destination end sends an acknowledgment packet to when the source end receives the acknowledgment packet.
One-way jitter | Delay variation from the source end to the destination end or from the destination end to the source end.
Number of error packets | Number of error packets during data transmission.
Description of TWAMP indicators
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 70: VPN Service Analysis and Assurance
The controller uses iFIT to implement proactive service SLA visualization and awareness and can proactively and quickly demarcate and locate faults, ensuring user experience.
  E2E mode: After the ingress (for example, PE1) of a VPN service is specified for iFIT E2E measurement initiation, PE1 inserts the iFIT E2E measurement header into the VPN service flow destined for PE2. PE1 and PE2 report the detection results respectively, and NCE computes and displays the E2E SLA.
  Hop-by-hop mode: For a VPN service with deteriorated quality, the system automatically triggers iFIT hop-by-hop measurement on the service ingress (for example, PE1). PE1 inserts the iFIT hop-by-hop measurement header into the VPN service flow destined for PE2, devices report the measurement results hop by hop, and NCE displays the nodes/links that cause poor service quality.
Controller
PE1
PE2
PE3
P3
P4
PE4
Service traffic
Delay
1
1
2
2
2
2
1
iFIT E2E measurement
2
iFIT hop-by-hop measurement
Data reporting within seconds through telemetry
Traffic Analysis
Quality Analysis
VPN Service Analysis
P1
P2

## Slide 71: Principles of VPN Service Analysis and Assurance
Analyzer obtains inventory data, including NEs, ports, links, and tunnels, from Manager.
Analyzer delivers the iFIT monitoring configuration and telemetry subscription configuration to NEs.
The unified southbound collection module collects NE iFIT performance data (including flow-related data) through telemetry and uploads the data to Analyzer.
Analyzer performs aggregation and calculation on performance data and displays the data to users from multiple dimensions, including topologies and reports.
1
2
VPN Service Analysis and Assurance
Management unit
NE
2
3
Visualized business
4
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 72: VPN Service Analysis and Assurance Deployment
Basic configuration: Configure 1588 clock synchronization or NTP time synchronization (only packet loss detection is supported), interconnect Manager and Analyzer, synchronize inventory data, and configure port performance indicator thresholds.
Per-flow detection enabling: Select the device to be monitored and enable the detection function.
VPN monitoring instance configuration: Select the VPN to be monitored.
E2E quality threshold configuration for iFIT flows: Configure a threshold for iFIT flows. When the indicator of an iFIT flow exceeds the threshold, hop-by-hop flow measurement will be triggered to quickly identify the abnormal indicator and faulty point.
Basic configuration
Per-flow detection enabling
VPN monitoring instance configuration
E2E quality threshold configuration for iFIT flows
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 73: Display of iFIT-measured Actual VPN Service Quality
After iFIT is deployed, the iMaster NCE-IP visualized analysis platform can clearly display the E2E delay and packet loss rate.
Traffic Analysis
Quality Analysis
VPN Service Analysis

## Slide 74
(True or False) TWAMP supports both one-way and two-way packet loss detection.( )
(Single-answer question) When VPN service analysis and assurance are deployed, which of the following modes is used by devices to report detection data?( )
  Telemetry
  SNMP
  IFIG
  BGP-LS
Notes: False
A

## Slide 75
Huawei's CloudWAN solution leads WANs into the intelligent cloud-network era.
NetEngine series high-end routers are based on Huawei-developed chips, an advanced SDN architecture, and a mature VRP software platform. They support smooth evolution of WANs.
iMaster NCE effectively bridges the gap between physical networks and business intents, and implements centralized management, control, and analysis of entire networks. It enables resource cloudification, full lifecycle automation, and data analytics-driven intelligent closed-loop management according to business and service intents. Additionally, it has open network APIs that support rapid integration with IT systems.
This course describes the fundamentals and procedures of network management, network traffic control, and network performance analysis based on iMaster NCE-IP. For more controller-related operations, see the related lab guide.