## Slide 1
Datacom
Shi Miaomiao/WX791350
2021.5.10
He Junjian/WX80230
New

## Slide 2: Huawei CloudWAN Solution O&M and Troubleshooting

## Slide 3
In the intelligence era, especially with the rise of 5G and cloud services, the bearer WAN faces structural challenges. With the rapid development of new services such as 4K/8K, ultra-HD video, and VR, data traffic on the entire bearer WAN increases 10-fold every 5 years. In the 5G era, connectivity of everything will bring even faster traffic growth. Increasing network complexity leads to low O&M efficiency and OPEX increase year after year. In addition, passive customer experience management is in urgent need of improvement in the experience-centric era.
These problems can be systematically solved only when a digital twin driven by the business logic and service intents of users is built over the physical network.

## Slide 4
Upon completion of this course, you will be able to:
  Describe the iMaster NCE-IP architecture.
  Describe the basic troubleshooting process.
  Use the controller for routine O&M.

## Slide 5
CloudWAN Solution Controller Overview
Routine O&M
Basic Troubleshooting

## Slide 6: Huawei CloudWAN Solution Controller
Cloud platform
Functions and features
Scenario-specific apps
Network infrastructure
Automation engine
Management
Control
Intent engine
Conversion
Verification
Awareness
Analysis
Analytics engine
Intelligence engine
Forecast
Suggestion
Product engineering (deployment, HA, O&M...)
Basic framework (service framework and middleware)
Common services (engineering, log, alarm, and security)
Unified portal
Business scenario apps
Network Management
Network Slicing
Service Programming
O&M scenario apps
Network Performance Analysis
Network Path Navigation
VPN Service Analysis and Assurance
iMaster NCE-IP is an innovative network cloudification engine of Huawei. Positioned as the brain of the future cloud-based network, it integrates functions such as network management, service control, and network analysis. It is the core enabling system that implements network resource pooling, network connection automation and self-optimization, and O&M automation.
iMaster NCE-IP is located at the management and control layer of the cloud-based network. On the one hand, it manages and controls the lower-layer network composed of IP, transmission, and access devices. On the other hand, it opens capabilities and enables services for the upper layer, supporting interconnection or integration with the OSS, BSS, and service orchestrators as well as quick, customized development of the application layer.
iMaster NCE-IP aims to build an intent-driven network (IDN) that is first automated, then self-adaptive, and finally autonomous.
Open APIs
Cross-layer
Cross-domain
Multi-vendor

## Slide 7: iMaster NCE-IP Features (1)
iMaster NCE-IP is a full-lifecycle network automation platform that integrates management, control, and analysis. It focuses on service automation, O&M automation, and network autonomy to support bearer WAN cloudification and digitalization.
Converged management and control, supporting smooth network evolution
Cloud-based deployment
Integrates traditional NMS and SDN controller functions.
Achieves unified management and control of SDN and non-SDN networks, leverages SDN network automation, maximizes legacy network values, and reduces technical difficulties and risks of network evolution.
Provides a unified cloud platform, user portal, and API gateway as well as unified installation, deployment, and upgrade, greatly simplifying O&M.
Adopts a microservice-based architecture, enabling scenario-specific on-demand deployment.
Bearer WAN
SDN devices
Traditional devices
Bearer WAN
Bearer WAN
Bearer WAN
iMaster NCE-IP

## Slide 8: iMaster NCE-IP Features (2)
Open programmability
Intelligent O&M
Provides standard RESTful APIs to connect to external systems.
Provides a DevOps-based tool platform to quickly customize innovative services based on flexible business scenarios and network technologies.
Collects network-wide data, and uses the big data platform to perform panoramic and in-depth analysis on the quality and traffic data of the entire network, achieving intelligent analysis and predictive maintenance.
Continuously verifies network design and configuration to ensure that the network accurately implements user intents and runs stably.
RESTful
SNMP
XML
FTP
Open APIs
Open NBIs
Telemetry (network data collection within seconds)
WAN
Uses the big data algorithm for intelligent analysis and proactive prediction based on a massive amount of data.

## Slide 9: iMaster NCE-IP Software Architecture
iMaster NCE-IP is a cloud-based system that uses a service-oriented software architecture. It is deployed on a virtualization platform and can be scaled flexibly. iMaster NCE-IP provides three logical modules (Manager, Controller, and Analyzer) and various scenario-specific apps based on a cloud-based platform to achieve flexible and modular deployment based on customer requirements.
Cloud platform
Product engineering
Basic framework
Common services
NETCONF
Telnet
SNMP
BGP-LS
SBIs
PCEP
FTP
Telemetry
RESTful
SNMP
XML
FTP
Open APIs
Basic applications
Value-added applications
Mobile transport
Apps
Unified portal
Manager & Controller
Analyer
Service management
MPLS optimization
PCEP
BGP-LS
IP optimization
Centralized path computation
Slice management
NE management
Route flooding
Anomaly detection
SLA monitoring
Traffic analysis
Fault diagnosis
Simulation analysis
Traffic forecast
Third-party device adaptation
Southbound programming framework
Big data engine

## Slide 10: Unified Portal
iMaster NCE-IP provides a unified user portal based on the unified cloud platform. This portal provides access to various apps, and these apps call the interfaces of underlying components to implement various functions.
Notes: Network Management: manages all Huawei transmission, IP, and access devices in a unified manner, implements visualized service management and E2E provisioning of cross-domain services, detects network faults in a timely manner, and effectively locates faults across domains to meet the requirements of network informatization development.
Alarm Monitor: allows network maintenance personnel to learn the operating status of the network in a timely manner through centralized alarm monitoring. Alarm management includes monitoring alarms, handling alarms, setting alarm monitoring/processing rules, and remotely sending alarm notifications.
Data Collection: provides data collection monitoring and management capabilities, covering dimensions such as collection indicators, collection instances, and collection tasks. This helps users effectively monitor the running status of the collector.
Network Path Navigation: manages network paths, computes and optimizes E2E forwarding paths, and centrally configures and manages network topology information to optimize network resource utilization.
Network Performance Analysis: serves as a center for network experience awareness, decision making, and big data analytics. It provides visualized management to help users monitor network traffic and quality in real time, detect the network change trend, and optimize the network, improving O&M efficiency and reducing OPEX.

## Slide 11
CloudWAN Solution Controller Overview
Routine O&M
Basic Troubleshooting

## Slide 12: Alarm Monitoring Overview
Alarm Management allows you to monitor and manage alarms and events reported by the system or managed objects. Alarm Management also provides a variety of monitoring and processing rules to meet requirements in different monitoring and processing scenarios. In this way, network faults can be efficiently monitored, located, and rectified.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 13: Alarm Categories
Category | Description
Current alarms | Current alarms include unacknowledged and uncleared alarms, acknowledged and uncleared alarms, and unacknowledged and cleared alarms.
Historical alarms | Historical alarms refer to acknowledged and cleared alarms.
Masked alarms | You can mask alarms that you do not need to pay attention to. Masked alarms are moved to the Masked Alarms list and will not be displayed in the Current Alarms list even if they are generated later.
Event alarms | Event alarms are of the lowest severity. They are used to inform users of event occurrence. Unlike fault alarms, event alarms do not need to be handled.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 14: Alarm Severities and Status
Status Type | Alarm Status | Description
Acknowledgment status | Acknowledged or unacknowledged | The initial acknowledgment status is unacknowledged. After users acknowledge an alarm because they plan to handle it, the alarm status changes to acknowledged. After users unacknowledge an alarm, the alarm status changes to unacknowledged. Users can configure rules to automatically acknowledge alarms.
Clearance status | Cleared or uncleared | The initial clearance status is uncleared. When the fault that causes an alarm is rectified, a clearance notification is automatically reported to Alarm Management, and the alarm status changes to cleared. For some alarms, clearance notifications cannot be automatically reported to the alarm management system. They must be manually cleared after the corresponding faults are rectified. The background color of cleared alarms is green.
Alarm Severity | Default Color | Description | Handling Policy
Critical |  | A service-affecting fault has occurred, and measures must be taken immediately. | Handle critical alarms immediately. Otherwise, services may be interrupted or the system may break down.
Major |  | A service-affecting fault has occurred. If the fault is not rectified, it will lead to a severe result. | Handle major alarms in a timely manner. Otherwise, important services will be affected.
Minor |  | Trivial impact has been caused on services, but corrective measures need to be taken to prevent more severe faults. | Identify causes and eliminate risks.
Suggestion |  | A potential or imminent fault is detected, but services are not affected currently. | Handle suggestion alarms based on network and NE running status.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 15: Internal Alarm Processing Flowchart
Internal alarm processing includes alarm masking, correlation analysis, and severity redefinition.
Alarm name redefinition
Alarm masking
Intermittent interruption/Flapping (preprocessing)
Alarm change
Alarm severity and type redefinition
Correlation analysis
Aggregation
Remote notification
Northbound filtering
Automatic acknowledgment
Alarm preprocessing
Alarm archiving to the database
Intermittent interruption/Flapping (post-processing)
Alarm merging
Real-time notification
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 16: Internal Alarm Processing Description (1)
Operation | Description
Alarm name redefinition | After receiving alarms, Alarm Management matches these alarms against name redefinition rules and modifies the names of alarms that meet these rules.
Alarm masking | Alarm Management discards alarms that meet the masking rules (such alarms are not saved to the database) or records these alarms in the masked alarm list. Alarm Management does not preprocess such alarms.
Intermittent interruption/Flapping (preprocessing) | Alarm Management records alarms that meet the intermittent interruption/flapping rules in the intermittent interruption/flapping alarm list. Alarm Management does not preprocess such alarms.
Alarm change | Alarm Management updates the current alarm information based on reported alarm changes, such as alarm clearing or severity modification.
Alarm severity and type redefinition | Alarm Management redefines alarms that meet severity and type redefinition rules.
Correlation analysis | Alarm Management marks alarms that meet the correlation rules as root/correlative alarms and processes the root/correlative alarms based on actions in the rules.
Aggregation | Alarm Management aggregates alarms that meet aggregation rules based on the aggregation action.
Remote notification | When an alarm that meets the remote notification rules is reported, Alarm Management sends an email or SMS message to notify the O&M personnel.
Northbound filtering | Alarm Management sends alarms that meet the reporting conditions to the upper-layer NMS.
Automatic acknowledgment | Alarm Management automatically acknowledges the alarms that meet automatic acknowledgment rules. Automatically acknowledged alarms are then recorded in the historical alarm list.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 17: Internal Alarm Processing Description (2)
Operation | Description
Alarm archiving to the database | Alarm Management records alarms processed through the preceding steps in the database. Alarms masked or moved to the historical alarm list during alarm preprocessing do not undergo post-processing.
Intermittent interruption/Flapping (post-processing) | Alarm Management analyzes alarms in the intermittent interruption/flapping alarm list and processes alarms that meet the intermittent interruption/flapping policy.
Alarm merging | Alarm Management merges alarms that meet the merging conditions.
Real-time notification | Alarm Management updates alarm information in real time on the alarm page.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 18: Alarm Page Overview
Used to acknowledge the current alarm
Used to clear the current alarm
Used to set masking rules
Set filter criteria.
Export the CSV file based on the current filter criteria.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 19: Setting Masking Rules
You can create masking rules to prevent events and alarms that do not require attention from appearing in event logs and current/historical alarms, respectively.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 20: Automatic Service Discovery
For running devices newly added to iMaster NCE-IP for management, you can use iMaster NCE-IP to automatically discover services on these devices. After NE data synchronization, existing services can be automatically discovered by iMaster NCE-IP.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M
Notes: Open the Network Management app and choose Service > Auto Service Discovery from the main menu. On the page that is displayed, expand Search Service by Policy and click Search Service by Policy.

## Slide 21: 360-Degree Service View (1)
The 360-degree service view provides comprehensive service information, such as service alarms, locking status, and specific paths. Moreover, this view allows you to perform operations such as service diagnosis and active/standby switching.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M
Notes: The 360-degree service view can be accessed from each service view:
  Open the Network Management app and choose Service > View > Dynamic Tunnel from the main menu. Click the 360 icon next to a service.
  Open the Network Management app and choose Service > View > SR Policy from the main menu. Click the 360 icon next to a service.
  Open the Network Management app and choose Service > View > L2 EVPN Service from the main menu. Click the 360 icon next to a service.
  Open the Network Management app and choose Service > View > MBGP L3VPN from the main menu. Click the 360 icon next to a service.

## Slide 22: 360-Degree Service View (2)
The diagnosis function provided by the 360-degree service view allows you to check service connectivity, demarcate service faults, and determine whether a fault is a bearer tunnel fault or service fault.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 23: 360-Degree Service View (3)
The 360-degree view for a VPN service allows you to directly check the 360-degree view for the corresponding bearer tunnel, enabling quick fault locating.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M
LSP information can be directly checked in the 360-degree view for the bearer tunnel.

## Slide 24: Device Maintenance
The controller delivers convenient device management, facilitating routine maintenance and fault locating for O&M personnel.
Telnet/SSH
Configuration synchronization
IP network maintenance and fault locating
Alarm query
Tunnel information query
Fault information collection
Performance monitoring
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 25: Remote Management
The Telnet/SSH login function allows administrators to run commands on the controller web UI to operate and maintain devices. In this case, the clients used by administrators do not need to be routable to devices.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 26: Fault Information Collection
Fault information collection collects device diagnosis information, including a large amount of device running status information. Such information can be used for device inspection and fault diagnosis.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 27: Performance Monitoring
Real-time performance monitoring allows you to view the performance data of devices in real time and customize the content to be displayed.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 28: System Maintenance (1)
On the management plane, you can maintain and manage the iMaster NCE-IP platform, view the running status of underlying nodes, servers, and databases, stop and restart related nodes and servers, and monitor the performance of the controller in real time.
iMaster NCE-IP management plane
Nodes
Relational database
Redis database
Service
Monitoring, management
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 29: System Maintenance (2)
On the management plane, you can view the status of each node, service, database, and process, and perform operations such as stop, start, and restart on these objects.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 30: O&M Dashboard
The dashboard displays a summary of system evaluation, risk, and service health information as well as a summary of monitored system resource indicator information for the current system, helping O&M personnel learn the system health status during system running and reduce running risks.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M
3
2
4
1
Notes: In the preceding figure, 1, 2, 3, and 4 provide the following capabilities:
  1: provides an overview of system status evaluation based on the number of current risks and risk levels.
  2: displays risks when system resource or service status anomalies are monitored.
  3: displays service health status, specifically, service operation statistics within the latest 1 minute.
  4: Displays system resource indicator status, specifically, the average value of each VM resource (CPU, memory, I/O, and network traffic) within the latest hour and the top 3 information.
The dashboard also provides the redirection function. In other words, you can click the risk, service health status, or system resource monitoring area to go to the corresponding details page.

## Slide 31: Unified Monitoring
The O&M dashboard module monitors the indicators of NCE service, process, node, database, and key middleware resources in a centralized manner. By analyzing resource indicators, this module can detect and resolve potential risks in a timely manner. For key resources, you can set thresholds to trigger alarms and handle exceptions promptly.
Function UI | Indicator
Node monitoring | Node CPU, memory, disk space, network indicators, and process status
Service monitoring | Service CPU, memory, number of threads, etc.
Database monitoring | GaussDB 100 V3 status, number of connections, etc.
Key middleware monitoring | Kafka and ETCD indicators
Service statistics | Number of operation times, operation duration, etc. The data is obtained based on the call chain statistics.
Risk and event threshold settings | Threshold settings for nodes: CPU, memory, I/O, packet loss rate, delay, etc. Threshold settings for databases: number of sessions, password expiration time, etc.
Alarm Monitoring
Service Maintenance
Device Maintenance
System O&M

## Slide 32: Typical Routine O&M Cases
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
A company's branches communicate with each other over the company's own bearer WAN. iMaster NCE-IP is deployed to manage the WAN and perform routine maintenance on the WAN.
Branch A
Branch B
: L3VPN

## Slide 33: VPN Service Monitoring (1)
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
To monitor the L3VPN service between branch sites in real time, use the VPN Service Analysis and Assurance app of iMaster NCE-IP to deploy iFIT-based VPN service detection to monitor the service from the ingress node to the egress node in real time.
Implementation principle: iFIT E2E measurement is enabled on the ingress node of the specified VPN service. The ingress node inserts the iFIT E2E measurement header into packets in the VPN instance's traffic flow destined for the egress node. The ingress node and egress node report the measurement results respectively, and iMaster NCE-IP computes and displays the E2E SLA.
Telemetry-based iFIT measurement result reporting
iFIT E2E measurement header
iFIT trace measurement header
VPN service analysis and assurance
Notes: Here, technologies such as in-situ Flow Information Telemetry (iFIT) are used to meet the SLA assurance and O&M requirements of VPN services, implement proactive and visualized service SLA awareness, and proactively and quickly demarcate and locate faults. This helps ensure user experience.

## Slide 34: VPN Service Monitoring (2)
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
1
2
Creating a VPN monitoring instance
Viewing the hop-by-hop status of a VPN service
Creating a VPN monitoring instance

## Slide 35: VPN Service Monitoring (3)
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
In the VPN list, drill down to the VPN service details.
Faulty links and nodes
The VPN Service Analysis and Assurance app allows network administrators to quickly locate faulty links and nodes when L3VPN services are faulty.

## Slide 36: Network Performance Analysis
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
In addition to VPN services, the network administrator of the company needs to perform routine O&M and monitoring on bearer WAN devices to detect abnormal devices in a timely manner. In this case, the network administrator can use the Network Performance Analysis app to perform routine monitoring and generate O&M reports.
Network performance analysis
Notes: As a center for network experience awareness, decision making, and big data analytics, the Network Performance Analysis app provides visualized management to help users monitor network traffic and quality in real time, detect the network change trend, and optimize the network, improving O&M efficiency and reducing OPEX.

## Slide 37: Performance Topology
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
The performance topology view provided by the Network Performance Analysis app allows you to build and manage the entire network topology and learn the networking and running status of devices. The color and status displayed for each device icon in the physical view help you learn the running status of the entire network in real time.
The network administrator can view device and link loads in the performance topology in real time. If a link or device is overloaded, the administrator can manually adjust tunnel paths to prevent services between sites from being affected.
Link congestion
The administrator manually performs local optimization after finding that a link is congested.

## Slide 38: Network Optimization
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
If a link or node is faulty, you can use the Network Path Navigator app to ensure L3VPN service continuity through network optimization. After selecting a faulty link, you can view tunnels carried over the link and schedule the bearer tunnel of the L3VPN service to another link.
Manually performing local optimization

## Slide 39: Maintenance Window (1)
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
The faulty node needs troubleshooting. If a device needs to be replaced, you can use the maintenance window function to ensure that services automatically bypass the target node during device replacement and service paths are automatically recomputed after device replacement. This allows the new device to take over service forwarding.
The Network Path Navigation app allows you to configure maintenance policies for NEs and links. After the maintenance starts, the system generates new service tunnel paths that bypass the maintained devices and links. After the maintenance is complete, the system performs path computation for traffic optimization.
Under maintenance
Path computation for traffic optimization after maintenance is complete

## Slide 40: Maintenance Window (2)
Background
VPN service monitoring
Network performance analysis
Network optimization
Maintenance window
1
Configuring a maintenance window
2
Under maintenance
When a device is replaced, tunnel paths bypass the node.
3
Tunnels switch back to original paths after the maintenance is complete.

## Slide 41
CloudWAN Solution Controller Overview
Routine O&M
Basic Troubleshooting

## Slide 42: Topology Management Fault (1)
Symptom: When an NE is added, a message indicating that the NE already exists is displayed.
Cause: The NE has been added to NCE.
Procedure:
  Open the Network Management app and choose Topology > View > Physical Topology from the main menu. Then click the search button next to the toolbar.
  Enter a keyword, such as an NE name or device type, and click the search button again.
  If the NE can be found in the search result, the NE has been added to NCE.

## Slide 43: Topology Management Fault (2)
Symptom: During automatic NE discovery, an SNMP NE is created as a third-party NE.
Cause: The agent corresponding to the SNMP NE is not enabled. As a result, the SNMP NE is created as a third-party ICMP NE.
Procedure:
  Log in to the management plane of iMaster NCE-IP.
  Choose Product > System Monitoring from the main menu. On the System Monitoring page, click the Processes tab and enter agent in the search box to filter processes.
  Check the status of the snmpagentservice process. If the process is not running, click Start to start the process.

## Slide 44: Topology Management Fault (3)
Symptom: After a user selects an NE on the web UI and clicks Ping on the information panel that is displayed, the ping operation fails, and a timeout message is displayed. However, the NE can be pinged through the CLI.
Cause: The built-in ICMP tool of iMaster NCE-IP is abnormal.
Procedure:
  Log in to the management plane of iMaster NCE-IP.
  Choose Product > System Monitoring from the main menu. On the System Monitoring page, click the Services tab and enter topology in the search box to filter services.
  Check the status of the topology service. If the service is not in the running state, click Start to start the service.

## Slide 45: Topology Management Fault (4)
Symptom: When a link is added, the corresponding connection fails to be created.
Cause: The NE is busy during data synchronization. As a result, some data fails to be synchronized.
Procedure:
  Change the Timeout Interval setting of SNMP.
  Open the Network Management app and choose System > NE Communication Parameters from the main menu. Then expand NE Communication Parameter and click NE Access Protocol Parameters.
  Double-click the SNMP record of the NE. In the detailed information area, increase the value of Timeout Interval (s).

## Slide 46: Failure to Obtain NE Alarm Information
Symptom: SNMP parameters have been set on NCE and an NE. NCE, however, fails to receive trap packets from the NE or does not process received trap packets. As a result, NCE cannot obtain NE alarm information.
Cause: The NE management address configured on NCE is different from the source address used by the NE to report trap packets.
Procedure:
  Delete the NE from iMaster NCE-IP. Specifically, open the Network Management app and choose Topology > View > Physical Topology from the main menu. In the topology view, right-click the NE and choose Delete from the shortcut menu.
  Add the NE again and set the NE address as the source address for sending trap packets.

## Slide 47: Failure to View Certain Alarms
Symptom: Alarms received by NCE cannot be found on the Current Alarms or Historical Alarms page.
Cause: Some alarms are filtered out because they meet the filter criteria or alarm template rules.
Procedure:
  On the page for browsing alarms, click Filter. In the Filter dialog box, view and modify the filter criteria.
  Then click OK.

## Slide 48: PCEP Session Interruption
Symptom: The PCEP session between the controller and a device is interrupted.
Cause: The source address configuration changes, the number of delegated LSPs exceeds the PCE limit, or the controller receives incorrect PCEP messages.
Procedure:
  Open the Alarm Monitor app and choose Current Alarms from the main menu.
  Click Filter and then click Alarm Name to display all alarms similar to PCEP_Session_Down.
  Locate the target alarm and click the alarm name to view alarm details.
  Check the possible causes one by one based on information displayed in the Possible Causes field on the alarm details page.
Notes: Possible causes:
  The network control node received incorrect PCEP messages. In this case, the peer end automatically re-establishes the connection, and you are advised to wait for some time. If the PCEP session is still down, contact technical support for the forwarder.
  The hold timer expired. In this case, you need to check the network connection between the controller and forwarder and restore the communication between them as required.
  The controller source address was changed. In this case, check whether the actual controller IP address is the same as the controller IP address configured on the forwarder. If they are the same, you are advised to wait for some time. If the PCEP session is still down, contact technical support for the forwarder.
  The number of delegated LSPs exceeded the PCE limit. Check the PCE delegation limit. Set the limit to a larger value or reduce the number of LSPs delegated by PCCs.
  Enable/disable TLS authentication. In this case, the value of Possible Causes is Enable TLS authentication or Disable TLS authentication. After PCEP TLS authentication is enabled or disabled on the forwarder as required, wait for the forwarder to re-establish the connection. If the PCEP session is still down, contact technical support for the forwarder.
  PCEP configurations were deleted. In this case, check the PCEP configurations on the controller and reconfigure PCEP as required.

## Slide 49: No Tunnel Delegated to the Controller
Symptom: The controller detects that no tunnel is delegated by PCCs.
Cause: Tunnel delegation is not configured on the forwarder.
Procedure:
  Open the Alarm Monitor app and choose Current Alarms from the main menu.
  Click Filter and then click Alarm Name to display all alarms about PCE sessions without delegated LSPs.
  Locate the target alarm and click the alarm name to view alarm details.
  Rectify the fault based on information displayed in the Cause and Suggestion field on the alarm details page.

## Slide 50
(Single-answer question) Which of the following device maintenance modes is not supported by iMaster NCE-IP?（）
  Remote management (Telnet and SSH)
  Fault information collection
  Remote file management
  Performance monitoring
Notes: C

## Slide 51
This chapter describes the logical architecture of iMaster NCE-IP, which provides various apps (such as Network Management, Network Path Navigation, Network Performance Analysis, and VPN Service Analysis and Assurance) based on a universal basic platform to meet the function requirements of different scenarios. Moreover, iMaster NCE-IP has good scalability.
This chapter also describes common O&M methods used by the controller, helping you understand how to maintain services through the controller and how to perform controller O&M through the management plane.
Finally, this chapter describes the common faults of the controller and their troubleshooting methods.